Tender for Supply of Equipments & Instruments for

Department of ANATOMY

Genetics Laboratory

At

BLDE (Deemed to be University)

Shri B.M.Patil Medical College, Hospital & Research Centre

Vijayapura

Supported by

Vision Group on science & Technology

Government of Karnataka

K FIST-L1 Programme

Through

e-Procurement

Government of Karnataka

https://eproc.karnataka.gov.in

Department of ANATOMY

Genetics Laboratory

BLDE (Deemed to be University)

Shri B.M.Patil Medical College, Hospital & Research Centre

Vijayapur- 586103

Ph: 08352- 262770

Last Date for submission of tender:          20/10/2018 Up to 05:30 PM

Time and Date of Opening of tender:       25/10/2018 at 04:00 PM

Place of opening of Tenders: 		Principal’s Office

BLDE (Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre

Vijayapur – 586103, Karnataka

Address for Communication: 		Principal,

BLDE (Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre

BLDE University Campus,

Vijayapur-586103, Karnataka

Ph: 08352- 262770, Fax: 08352-263303

E-mail: bldeascop@yahoo.com

Invitation for Tenders (Through e-Procurement Only)

(Tender Notification)

The Department of Anatomy Genetics Laboratory of BLDE(Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre, Vijayapur is planning to establish the laboratory facilities for the study on “Molecular Characterization of NOS1 Gene in Parkinson Disease” under the financial assistance from Vision Group on Science and Technology (VGST), Government of Karnataka through a grant: K FIST-L1

In view of this, tenders are invited from reputed firms to supply/install the listed equipments/instruments.

- BLDE(Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre, Vijayapur, Solapur Road, Vijayapur - 586103 invites tenders from eligible tenderers for the supply of above mentioned equipments and instruments. The tenderers may submit tenders for the supply of said instruments and equipments.

- Tender documents may be downloaded from Government of Karnataka e-Procurement website https://eproc.karnataka.gov.in  from 05/07/2018.

- Tenderer should pay the Earnest Money Deposit (EMD), and tender processing fee, which shall be paid online through e-Procurement Portal using any of the following Payment Modes: Credit Card, Direct Debit, National Electronic Fund Transfer (NEFT), and Over the Counter (OTC).

- Tenders must be electronically submitted (online through Internet) within the date and time prescribed in e-Procurement Portal. Bid Cover of the tender will be opened at the prescribed time and date as mentioned in the e-Procurement Portal in the presence of the tenderers at BLDE(Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre, Vijayapur, Solapur Road, Vijayapur-586103. Other details can be seen in the tender documents.

Calendar of Events

- Last date for uploading the filled tender Document is as per e-procurement portal:20/10/2018 up to 05:30 PM---

- The date of opening of bids as per e-procurement portal: 25/10/2018 at 04:00 PM

Tender for Supply of

| Sl. No | Name of Equipment & Instrument | Quantity | Details of Technical Specifications as proposed in the e-procurement document | EMD Amount (Rs) |
| --- | --- | --- | --- | --- |
| 1 | PCR | 01 | 96 wellx0.2ml PCR tubes/one 96 well plate, Gradient PCR= capable of testing 12 different temperatures simultaneously across a gradient range of 1-25 °C and a temperature gradient from 30-100ºC, with minimum 0.1ºC increment in gradient Peltier based heating and cooling, Thermo block made of silver Should be capable of testing temperatures at Denaturation, Annealing & Extension steps Block ramp rate: 4-5.0ºC/Sec. Average ramp rate °C/sec 2.5-3. Temperature range 0-100ºC/S Temperature accuracy: Adjustabrate:4.4ºC/S Temperature range 0-100ºC/S Temperature accuracy: ±0.5ºC Temperature uniformity ±0.5°C well-to-well within 30 sec of arrival at target temperature Display 5.7'' VGA color touch screen Memory 500 typical programs; unlimited with USB flash drive expansion | 8000/- |
| 2 | Horizontal Gel Electrophoresis | 01 | Cell size (W x L x H) 9.2 x 25.5 x 5.6 cm Gel tray sizes (OD) (W x L) 7 x 7 cm 7 x 10 cm Ready Agarose™ gels accommodated Yes, 8-, 12-, 2 x 8-well Sample throughput 8–30 Base buffer volume ~270 ml Buffer recirculation No Bromophenol blue migration ~4.5 cm/hr (at 75 V) QuickSnap* electrodes are easy to remove, simplifying cleaning Arrow on the side of the base indicates the direction of the run and ensures proper orientation of the gel Color-coded, labeled electrodes and labeled base guarantee correct positioning of the lid on the base Tabs on the base permit easy removal of the lid, reducing buffer spillage, and also prevent incorrect lid positioning Reverse-compatible design allows the cells to be used with components from older models Clear plastic construction for easy sample visualization UV-transparent gel trays with fluorescent ruler** Gel-casting gates to cast your own gels right in the cell, or optional caster for tape-free casting** Combs to fit every need (fixed-height drop-in combs, adjustable-height combs, and preparative combs)** Power Pack Output range (programmable) 10–300 V, fully adjustable in 1 V steps 4–400 mA, fully adjustable in 1 mA steps 75 W (maximum) Type of output Constant voltage or constant current with automatic crossover Output terminals 4 pair recessed banana jacks in parallel Regulatory EN-61010, CE Safety features No-load detection, sudden load change detection, overload/short-circuit detection, overvoltage protection Input protection Fuse on both hot and neutral | 2000/- |
| 3 | -20 ºC Deep Freezer | 01 | Technical Specifications Capacity 280 liter Microprocessor controller for precision temperature with digital( display Temperature set range from -10 to -25 deg C( Audible and visual alarm( Dimensions : Internal (mm) 435 X 440 X 1575( External (mm) 595 X 680 X 1850( Interior ABS Plastic( Exterior Pre-painted steel( Lockable door with door handle( Shelves 07 No’s( External door 01 No( CFC Free refrigerant R134a( Manual defrost(Alarm and Safety: Multiple failure alarm system : High and low temperature alarm( Audible/visual Alarm System. System Performance Fast pull down and temperature recovery( Less power consumption( Including Voltage stabilizer | 2000/- |
| 4 | Cold Centrifuge | 01 | Cold Centrifuge: Specifications Max. Speed 15000rpm(200-15000rpm), increment:10rpm Max. RCF 21380×g, increment:10×g Speed Accuracy ±20 rpm Temperature Range -20oC-40oC Rotor Capacity 5mL×18, 5mL culture tubex12 0.2mL/0.5mL/1.5mL/ 2mL×24, 0.5mL×36, PCR8×4 Run Time 30sec-99min/Continuous Motor Brushless DC moto Safety Devices Dual door interlock, Over-speed detection, Over-temperature detection, Automatic internal diagnosis Power Single-phase, AC220V-240V, 50Hz/60Hz, 10A, AC110V-120V, 50Hz/60Hz, 10A 400W Acceleration /Braking time [Sec] 25s↑25s↓ Dimension [D×W×H] 338×580×324mm Weight 30kg Certification CE cTÜVus FCC MCA Advanced Features Speed/RCF switch; Short-time run function; sound-alert function Powerful cooling system for precise temperature control Pre-cooling program ensures optimal protection of the sample before warming Guaranteed 2°C cooling within only 7 minutes of both chamber and samples even at maximum speed and capacity utilization Sound-alert allows your undivided attention on other tasks warming Lid lock facility allows for internal temperature maintenance even after centrifugation Intermittent temperature control mode, CFC-free refrigerant and low carbon life rotor capacity Bio-safe rotor/anti-sample overflow prevents accidental leakage during centrifugal process allowing risk-free microbial contamination High strength aluminum alloy rotor can be fully autoclaved for unlimited service life Rotors Including complete with 24 place 1.5/2.0mL Quiet running, noise level ≤ 54dB | 2000/- |
| 5 | UV Transilluminator | 01 | UV source 365 nm Wave Length Viewing area 24 x 14 cm UV Tube 4x8 watts UV Tube Housing Anti Corrosion treated with Powder coated Mild Steel UV Safty Shield Clear Transparent lid for excellent clarity Input 220V AC, 50-60HZ Fuse 1 Amp | 4000/- |

Technical Bid: The Technical bid shall cover following documents:

- The successful tenderer shall enter into the agreement with BLDE (Deemed to be University) Shri B.M.Patil Medical College, Hospital & Research Centre, Vijayapur-586103, within seven days of receipt of intimation. The tender document will form the part and partial of the agreement.

- BLDE(Deemed to be University)University’s Shri B.M.Patil Medical College, Hospital & Research Centre, Vijayaur-586103, reserves the right to reject any or all of the tenders without assigning any reasons and without any liability or obligation to inform the tenderers of the reasons for such action. The quantity may also vary according to the requirements.

- The tender rate will remain valid for a period of 180 days from the last date prescribed for submission of tender. The duration of the contract may be extended for further period of six months on mutual agreement but without variation of price.

- The supply shall be made as per schedule quoted in their tender by the vendor from the date receipt of the supply order failing which loss caused to the Institution will be recovered from the vendor.

- Warranty for instruments shall be three years.

General Conditions and Financial Bid

- The participants shall produce all the original documents for verification whenever necessary.

- Tender documents shall be submitted in the prescribed format after downloading the same from e-procurement portals. \\

- Scanned Brochures /Information / Profile of the firm shall be submitted.

- Company registration certificate and VAT registration certificate.

- The Instruments shall be supplied to the Places/Departments/Offices as may be specified in the supply order.

- No advance payment will be made for the supply of materials.

- Not withstanding anything contained in KTPP Act and rules the institution reserves the right to modify the quantity or cancel the whole tender.

- Filled in applications shall be submitted through on-line within the dates specified.

- Institution reserves the right to depute an Expert Committee to verify the facilities / or the information furnished by the vendor is as per the tender document or would meet the requirements of Institution.

- Lowest bidder will be evaluated as per KTPP Act 2000 and also keeping in view with their technical expertise, the facilities available past experience, financial stability, track record of the firm and such other relevant information.

- The specification shall be as mentioned in the tender document. Rate inclusive of tax.

- “Appropriate methods will be adopted by the institution to ensure the quality” of the materials used in the manufacturing and such assessment of quality is binding on the vendor.

- In case of the material supplied is not inconformity with the specification or raw materials is used for the manufacturing of the materials is found to be of lesser quality than the specified, such materials will be rejected and any loss sustained by the institution on this account will be recovered from the vendor.

- Payment will be made only after quality certificate issued by the expert appointed by the Institution.

- Conditional tenders will not be accepted. Wherever the word Vendor or tenderer appeared it shall be treated as single entity.

- The tender notification will be accessible in the e-Procurement website (www.eproc.karnataka.gov.in).

- Any technical clarifications for e-procurement, please contact help desk.

Technical document shall contain following documents:

- The tenderer shall have supplied successfully the equipments to Government or autonomous institutions. In support of this, the tenderer shall furnish Certificates duly certified by the competent authority along with the document bid. In case of supply to institution he is exempted from production of one certificate.

- Local Service Centre is mandatory and it shall be located in Bangalore. Documentary evidence for existence of service center shall be produced along with Man power, Spare parts stock, and stand by facilities in the service center.

- The instruments proposed shall be inclusive all technical specifications indicated in the tender document.

Commercial document shall contain following documents:

- Price including all taxes.

- Splitting of price is not allowed.

- Price should be inclusive of delivery to institution and installation.

- General Profile of the company.

Tender evaluation scoring system:

- An Expert Committee will be constituted for tender valuation.

- Only technically valid tenders will be considered for financial comparison.

- Price is not sole criteria for determination of lowest bidder.

- Technical and commercial rating will be considered for final recommendation.

- Technical equivalence, technical rating and commercial rating will be established by the expert committee.

- Man Power and Expertise.

Programme co-ordinator						             Principal

Dr. R S Bulagouda							     Dr. S P Guggarigoudar