本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

SyncSort MVS Programmers Guide

All rights reserved. This document contains proprietary and confidential material, and is only for use by lessees of the SyncSort MVS proprietary software system.

R O V E N performance

MVSTMProgrammer's GuideRelease 3.7SI-0101-ASyncsort is a registered trademark of Syncsort Incorporated

[此处图片未下载成功]

&#169; Syncsort Incorporated, 1998

rights reserved. This document contains propri-

and confidential material, and is only for use by

of the SyncSort MVS proprietary software

. This publication may not be reproduced in

or in part, in any form, except with written

from Syncsort Inc.

MVS is a trademark of Syncsort Incorporated.

other company and product names used herein

be the trademarks of their respective companies.

of Contents

1.Introduction . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . . . .

Introduction to SyncSort MVS . . . . . . . . . . . . . . . . . . . . . . . . . . . .

's Basic Functions . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

's Data Utility and SortWriter Features . . . . . . . . . . . . . . . .

SortWriter Report . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Environment Support . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

2000 Support . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

's Operational Features . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

's Value-Added Products . . . . . . . . . . . . . . . . . . . . . . . . . . . .

of the Programmer's Guide . . . . . . . . . . . . . . . . . . . . . . . . .

Reading . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . . . . . . . . . . . . . . . . .

Message Help . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .1.11.11.11.31.41.51.51.51.51.61.71.8

2.SyncSort Control Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.1

Statement Summary Chart . . . . . . . . . . . . . . . . . . . . . . . . . . .2.3

Sort, MAXSORT, PARASORT and Tape Sort Control Statement

. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.5

Utility Processing Sequence . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.6

Statement Examples . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.8

for Control Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.8

Control Statement . . . . . . . . . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . .2.13

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.15

/OMIT Control Statement . . . . . . . . . . . . . . . . . . . . . . . . .2.16

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.30

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.32

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.43

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.47

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.48

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.74

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.103

Control Statement . . . . http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.107

Control Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .2.121

3.How to Use SyncSort's Data Utility Features . . . . . . . . . . . . . . . .

. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Data Utility Applications . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Input Records . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Relevant Fields from the Input Records . . . . . . . . . . . . . . . .3.13.13.23.33.6

of Contentsi

Records within a File . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Output Records Printable and Easy to Read . . . . . . . . . . . . .

a Report into Sections . . . . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . .

Headers and Trailers for a Report . . . . . . . . . . . . . . . . . . . .

and Subtotaling Data . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Maximum, Minimum and Average Data . . . . . . . . . . . . . .

Data Records . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Multiple Output Files . . . . . . . . . . . . . . . . . . . . . . . . . . . . .3.113.133.293.313.393.453.473.51

4.JCL and Sample JCL/Control Statement Streams . . . . . . . . . . . .4.1

Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.3

MAXSORT, PARASORT and Tape Sort . . . . . . . . . . . . . . . . . . . .4.3

Conventions for DD Statements . . . . . . . . . . . . . . . . . . . . . . .4.3

/JOBLIB DD Statement . . . . . . . . . . . http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . . . . . . . . . . . . . . . .4.4

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.4

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.5

or SORTINn DD Statement . . . . . . . . . . . . . . . . . . . . . . .4.7

, SORTOFxx, SORTOFx and SORTXSUM DD Statements .4.8

or SORTWKn DD Statement . . . . . . . . . . . . . . . . . . . . . .4.9

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.11

$ORTPARM DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.11

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .4.14

Exit Routines that Require Link-editing at Execution Time . . . .4.14

Statements for MAXSORT, PARASORT and Tape Sort . . . . . . . .4.16

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aple JCL/Control Statement Streams . . . . . . . . . . . . . . . . . . . . . .4.16

5.PARM Options . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.1

MAXSORT PARMs . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.1

PARM . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.2

Tape Sort PARMs . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.2

Rules . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.2

Option Summary Chart . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.2

PARM Options . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .5.7

Accepted But Not Processed by Disk Sorts . . . . . . . . . . . . . .5.33

6.Invoking SyncSort from a Program . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . . . . . . . . .6.1

Flexibility vs. Performance . . . . . . . . . . . . . . . . . . . . . .6.1

Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .6.1

the Sort/Merge from an Assembler Program . . . . . . . . . . . . .6.2

24-Bit Parameter List . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .6.4

Assembler Invocation Using 24-Bit Parameter List . . . . . . . .6.12

31-Bit Extended Parameter List . . . . . . . . . . . . . . . . . . . . . . . . .6.13

Assembler Invocation Using 31-Bit Parameter List . . . . . . . .6.18

7.The Coding and Use of Exit Programs . . . . . . . . . . . . . . . . . . . . . .7.1

Is an Exit? . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.1

the Exit Routines into Main Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atorage . . . . . . . . . . . . . . . . . . .7.3

Conventions . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.3

Conventions . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.4

Exit Communication Area . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.4

E11, E21, and E31 - Preparing for Other Exit Routines . . . . . . .7.5

E32 - Invoked Merge Only: Creating Input Records . . . . . . . . . . .7.5

E14, E15, E25, and E35-Deleting, Creating, and Changing Records7.7

E14 - Deleting, Summarizing, Changing Records . . . . . . . . . . . . .7.7

E15 - Creating, Revising or Analyzing the Input File . . . . . . . . . .7.8

a COBOL E15 Exit Routine . . . . . . . . . . . . . . . . . . . . . . . . . .7.10

1: Fixed Length Records . . . . . . . . . . . . . http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . . . . . . . . . . . . .7.11

2:Variable Length Records . . . . . . . . . . . . . . . . . . . . . . . .7.12

a C E15 Exit Routine . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.19

Length Records - Function Definition . . . . . . . . . . . . . . . . . . .7.20

Programmer'sGuide

Length Records - Function Definition . . . . . . . . . . . . . . . . .

E25 - Deleting, Changing, Summarizing Records . . . . . . . . . . . .

E35 - Adding, Deleting and Changing Records . . . . . . . . . . . . . .

a COBOL E35 Exit Routine . . . . . . . . . . . . . . . . . . . . . . . . . .

a C E35 Exit Routine . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Length Records - Function Definition . . . . . . . . . . . . . . . . . . .

Length Records - Function Definition . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . .

E16-Taking Action on Insufficient Intermediate Storage . . . . . .

E17, E27, and E37 - Closing Data Sets . . . . . . . . . . . . . . . . . .

E18, E38, and E39 - Checking Labels, Processing Read or Write

, End-of-File Routines, Special VSAM Processing . . . . . . . . . .

E61 - Modifying the Collating Process . . . . . . . . . . . . . . . . . . . .

REXX Exits . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .7.217.277.287.307.437.437.457.517.527.527.567.58

8.The Flow of the Sort . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .8.1Chapter 9.MAXSORT . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.1

: A Maximum Capacity Sort . . . . . . . . . . . . . . . . . . . . . . . .9.1

's Advantages . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . . . . . . . . . . .9.4

Control Language . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.4

Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.4

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.6

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.7

DD Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.8

Disk for Intermediate Output . . . . . . . . . . . . . . . . . . . . . . . . . .9.9

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.10

Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.10

Options . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . .9.10

Programs . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.14

MAXSORT from a Program . . . . . . . . . . . . . . . . . . . . . . . .9.14

MAXSORT . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.14

's Operator Interface . . . . . . . . . . . . . . . . . . . . . . . . . . . .9.15

MAXSORT JCL/Control Streams . . . . . . . . . . . . . . . . . . . . .9.18

10.PARASORT . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

: Parallel Input Processing for Elapsed Time Improvement

Applicability . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Control Language . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Statements . . . . . . . . . . . . . . . . . . . . . . . . http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . . . . . . . . . . . . . . . .

DD Statement with PARASORT . . . . . . . . . . . . . . . . . . . . .

DD Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Channel Separated Esoteric Names . . . . . . . . . . . . . . . . . . . .

Considerations . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Notes . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

11. Tape Sort . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

to Use Tape Sort . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

DD Statemenhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

$ORTPARM DD Statement . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Tape Sort . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Statements . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Programs . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Tape Sort Through JCL/Control Streams . . . . . . . . . . . . . .

Tape Sort from a Program . . . . . . . . . . . . . . . . . . . . . . . . .10.110.110.110.210.210.310.510.710.810.911.111.111.211.311.411.411.511.511.711.811.811.10

12. Performance Considerations . . . . . . . . . . . . . . . . . . . . . . . . . . . .12.1

http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSort? MAXSORT? PARASORT? Tape Sort? . . . . . . . . . . . . . . . .12.1

of Contentsiii

Sorts vs. Program-Invoked Sorts . . . . . . . . . . . . . . . . . . . . . . . .

Statement Issues . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Efficient Use of PARMs . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

System Resources . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

CORE . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Incore Sort . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Space Considerations . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Coding and Use of Checkpoint-Restart . . . . . . . . . . . . . . . . . . . .

Checkpoint-Restart . . . . . . . . . . . . . . . . . .http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a . . . . . . . . . . . .

Checkpoint-Restart . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Data Set Placement . . . . . . . . . . . . . . . . . . . . . . . . . . . .12.212.212.312.412.412.612.712.1012.1212.1312.14

13. The HISTOGRM Utility Program . . . . . . . . . . . . . . . . . . . . . . . . .13.1

Is HISTOGRM? . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .13.1

HISTOGRM to Determine L6 and L7 Values for SyncSort . . .13.2

Parameters for HISTOGRM . . . . . . . . . . . . . . . . . . . . . . . . .13.2

Control Language . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .13.4

HISTOGRM through an E15 Exit . . . . . . . . . . . . . . . . . . .13.5

Messages . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .13.10

14http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. Value-Added Products . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

/COBOL Advantage . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

SYNCSORT - An Accelerator for SAS&#174; Sorting . . . . . . . . . . .

. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

15. Messages . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Statistical Record Facility Messages . . . . . . . . . . . . . . . . . .

SYNCSORT Messages . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

(KEY) Messages . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

Abends . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .

.114.114.214.215.115.4915.4915.5015.51 . . . . . . . . . . . . . . . . http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .I.1

Programmer'sGuide

MVS Release 3.7 - Summary of ChangesPerformance Improvements

algorithmic and optimization enhancements have been made that improve sortingCPU time and elapsed time.Specific enhancements include:

Up to 15% reductions in CPU time for COBOL-invoked sorts.Elapsed time improvements for sorts with SORTWK data sets allocated to extremely

devices.

time and EXCP improvements when input or output data sets are non-

Extended Format Data Sets.

with input tapes controlled by DFSMSrmm may realize CPU time im-

of up to 20%.The most dramatic reductions in CPU time will be for the

:

Applications whose input files contain significantly less data than the tape ca-pacity.When compressionhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a is used but a low level of compression is actually achieved.

obtain these improvements, the following IBM PTFs must be applied to

:

DFSMSrmm 1.3 - PTF UW47006DFSMSrmm 1.4 - PTF UW47007

Performance Feature

PARASORT technique has been added.PARASORT improves elapsed time perform-ance for sorts whose input is a multi-volume tape data set and/or concatenated tape datasets.Reduced elapsed time can help critical sort applications achieve batch window goals.The performance improvement from PARASORT is a result of processing the SORTINinput volumes in a parallel fashion.Depending upon the resources provided, elapsed timecan be reduced up to 20% for 2-way input and up to 33% for 4-way input.

of Changesv

Utility Features

SyncSort MVS data utility features have been enhanced with the following:

INCLUDE/OMIThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a and OUTFIL INCLUDE/OMIT Statements

The comparison feature (COND=comparison) now provides substring comparison,

allows the search for a constant within a field or for a field value within a

.Substring comparison is implemented via a new format, SS.

/OMIT has been enhanced to support 2-digit year fields for century-

comparisons.See &quot;Year 2000 Enhancements,&quot; below.

constants used for INCLUDE/OMIT comparisons can now be up to

characters in length, representing a 256-byte constant for compare.The

length limit was 256 characters, representing a 128-byte constant.

=ALL and COND=NONE have been added to the existing comparison fea-

(COND=comparison) for the INCLUDE/OMIT statement.COND=ALL in-

or omits all the input records.COND=NONE includes or omits none of the

recordshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.

INREC, OUTREC and OUTFIL OUTREC Statements

INREC/OUTREC can now be used for arithmetic calculations (plus MIN/MAX

) between fields within a record, between such fields and constants, and

constants.This feature can be viewed as &quot;horizontal arithmetic&quot; com-

the &quot;vertical arithmetic&quot; already available with SUM and the arith-

parameters of OUTFIL (TOTAL, MIN/MAX, and AVG).

/OUTREC has been enhanced to support conversion of numeric data to

numeric format.For example, it is now possible to convert ZD to PD

.Previously only numeric data conversion to a printable ZD field was

.Data conversion is now possible to any of the following formats:BI,

, CSF/FS, PD and ZD.

SEQNUM function has been added.It is used to insert a sequence number

within the record.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aWhen used with INREC, the sequence numbers reflect

order of records presented for INREC processing.When used with OUTREC

OUTFIL OUTREC, the sequence numbers reflect the order of records pre-

for OUTREC or OUTFIL OUTREC processing.

CHANGE subparameter can now be specified on the INREC or OUTREC

statement.Previously it could be specified only on OUTFIL OUTREC.

that this capability was provided with Release 3.6 TPF 5 maintenance.

edit patterns M10 through M25 have been added.

data formats have been added to support Year 2000 processing.See &quot;Year

Enhancements,&quot; below.

Programmer'sGuide

CSF or FS fields are now eligible for data conversion.In addition, data conversion

of FI fields has been enhanced to support field lengths of 1 to 4 bytes.

only 2 or 4 byhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ates were supported.

OUTFILStatement

Headers and Trailers can now contain user-formatted dates.The

&amp;DATE=(m1m2m3m4) subparameter has been added to generate the current date

formatting.You can specify the position of the year, month and date, specify

separator character, and choose between 2-digit and 4-digit year representation.

and Trailers can now contain user-formatted time.The &amp;TIME=hp

has been added to generate the current time with formatting.You

print the time in 24-hour or 12-hour formats and specify the separator char-

between the hours, minutes and seconds.

, ENDREC, and SAVE parameters have been added.They select re-

in bulk for OUTFIL processing:

STARTREC specifies the record number of the records presented for OUTFIL

that is to be the first record operated http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aupon for the OUTFIL spec-

.All records prior to this will be ignored for the OUTFIL group.

specifies the record number of the records presented for OUTFIL

that is to be the last record operated upon for the OUTFIL spec-

.All records after this will be ignored for the OUTFIL group.

specified for an OUTFIL group causes any record that has not been

in another OUTFIL group to be included for processing in the

group for which SAVE is specified.

Subparameters have been added to the TRAILER parameters (TRAILER1,

and TRAILER3) to generate additional printable numeric values.

, MAX and AVG generate the minimum, maximum or average numeric value

an input field for all records within a report, logical page or section.SUBMIN,

and SUBAVG generate the running (cumulative) minimum, http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amaximum

average numeric value of an input field for all records up to the end of the re-

, logical page or section.

the TOTAL/SUBTOTAL subparameter of the TRAILER parameters, the

length of the totaled field has been increased to 15 digits for BI and FI

formats.The previous limit was 10 digits.

TOTAL/SUBTOTAL subparameter may now refer to CSF or FS fields.

new subparameters, COUNT15 and SUBCOUNT15, have been added to the

parameter.These functions are identical to COUNT and SUBCOUNT

provide 15 digits.COUNT and SUBCOUNT are limited to 8 digits.

FNAMES parameter has been added.FNAMES connects the OUTFIL

with one or more output files.The files specified on this parameter

of Changesvii

with any specified on the FILES parameter will constitute the ddnames to

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arreceive output for the OUTFIL specification.

Each SECTIONS control field no longer requires a subparameter.This allows

non-contiguous control fields to be specified for each SECTIONS break

.

SORT and MERGE Statements

CENTWIN option was added to the SORT and MERGE control statements, andyear-related data formats were added.See &quot;Year 2000 Enhancements,&quot; below.

Processing

ZDPRINT/NZDPRINT option has been added.This option specifies if positive ZDsummation results are to be converted to printable numbers.ZDPRINT, the default, en-ables conversion to printable format.NZDPRINT prevents the conversion.Previously,conversion to printable numbers could not be turned off.

Counting

The EXTCOUNT PARM option has been added.EXTCOUNT enables special proc-

to accommodate applications that have record counts that exceed SyncSorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a'sdefault internal limit.By default, the internal limit on the number of records that canbe sorted for variable length data or for a sort application that uses the EQUALS op-tion is 4,294,967,295 records.Specifying EXTCOUNT increases the internal limit to140,737,488,355,327 records.Fixed length sorts without EQUALS, and all mergesand copies, have automatic support for the maximum number of records allowed bythe EXTCOUNT parameter.

that provide information on record counts or filesize can now print 15 digitsif needed.The previous limit was 10 digits.For compatibility with prior releases, thelength of the record count field in the message will continue to be 10 digits if the re-cord count or filesize is less than 4,294,967,295.For record counts equal to or greaterthan this number, the length of the record count field will be 15 digits.The messagesaffected are WER047A, WER054I, WER055I, WER159A, WER246I and WER405I. ://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarFile Processing

now supports a variable length (VL) SORTIN concatenation with increasingLRECLs if the LRECL can be determined at sort initiation.Message WER108I has beenmodified to indicate the largest LRECL of the concatenation, not the first.

Programmer'sGuide

File Processing

For an application that has no SORTIN (E15 only) and a variable length output file

a RECFM specification, SyncSort will now select a VB record format.Previ-ously, unblocked RECFM=V was selected.This enhancement provides improvedperformance by allowing the selection of a blocksize that is appropriate for the outputmedia.

an application that has a VSAM SORTIN and a non-VSAM output file:

If the output file does not have a RECFM specification, SyncSort will now select

blocked RECFM.Previously, unblocked output was generated.

the output RECFhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aM is blocked with no BLKSIZE having been specified and SDB

(system determined blocksize) is not in effect, an appropriate output BLKSIZE

be chosen for fixed length data, and the SORTIN control interval size will be

as the output BLKSIZE for variable length data.Previously, the record

(or record length  4) was used as the output BLKSIZE.

When there is no OUTFIL control statement, an output file that is defined to a JES

set for a sort application will now employ SDB (system determined blocksize) toselect an output blocksize.

The number of SORTWKs that can be provided to a non-MAXSORT sort application

been increased from 32 to 100.Up to 100 SORTWKs can be specified by the JCLand/or the DYNALLOC parameter.

sort application that uses OUTFIL and does not provide JCL SORTWKs can nowhave DYNALLOC automatically enabled.This will alhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1alow the completion of a sort thatmight otherwise terminate due to lack of required SORTWK space.

Processing

E15 exits are now supported in copy applications.

WER351I message, which reports the datasize for an individual MAXSORTSORT/MERGE, has been amended to display the datasize in 1024-byte units.Previouslythis value was displayed in 1000-byte units.

of Changesix

Processing

$ORTPARM, PARMEXIT and PARMTABLE now allow up to 256 bytes of PARMs to

passed to SyncSort.The previous limit was 100 bytes.

can now be invoked more than once in the same job step with different$ORTPARMDD control data sets for each invocation.Each data set can now be de-fined as a disk data set (or partitioned data set member) and defined in the JCLstream in the desired order with the FREE=CLOSE parameter added.This capabil-ity, which is onhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aly available in a JES2 environment, can be useful for COBOL Year2000 applications with multiple sort invocations.See &quot;Year 2000 Enhancements,&quot;below.

Programs

E15 and E35 user exits can now be written in C.

2000 Enhancements

2000 enhancements have been delivered in Release 3.6 TPF 4, Release 3.6 TPF 5 anddirectly in Release 3.7.

following describes Year 2000 capabilities included in Release 3.6 TPF 4 maintenance: The CENTWIN PARM option has been added.CENTWIN defines a sliding or fixed

-year window that determines the century to which 2-digit year data belongs whenprocessed by SORT, MERGE, INREC, OUTREC or OUTFIL OUTREC control state-ments.

date data formats have been added: Y2C, Y2D, Y2P and Y2Z.These data for-mats define a 2-digit year value that is to be treated as a 4-digit year.They are usedin conjunction with the CENTWIN option, which specifhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aies a century window that isapplied to the 2-digit year data specified with the date data formats.The new dataformats can be specified on SORT or MERGE control statements to correctly collate2-digit years that span century boundaries, or they can be specified on an INREC,OUTREC or OUTFIL OUTREC control statement to convert 2-digit years to 4-digitprintable output.

addition, two date formats have been added for year conversion with INREC,OUTREC and OUTFIL OUTREC.These formats (Y2ID and Y2IP) are used withCENTWIN to expand a 2-digit year in packed decimal format to a 4-digit year.Thepacked decimal format is maintained in the output field.

A new data format, PD0, has been added.This format, which defines packed decimal

, ignores the first digit and trailing sign during processing.PD0 is normally usedin conjunction with the Y2P data format.The Y2P is used to process the 2-digit yearportion of a packed decimhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aal date field, while the PD0 format is used to process themonth and day portion of the field.

Programmer'sGuide

following describes Year 2000 capabilities included in Release 3.6 TPF 5 maintenance: Century evaluation can now be applied to INCLUDE/OMIT or OUTFIL

/OMIT comparison conditions involving 2-digit year data.For example,without CENTWIN processing, an INCLUDE/OMIT comparison would treat the year01 as &quot;less than&quot; the year 98.With CENTWIN processing, the 01 field could be re-cognized as a twenty-first century date (2001), which would be treated as &quot;greaterthan&quot; 98 (1998).The data formats applicable to INCLUDE/OMIT processing are PD0and the year data formats Y2B, Y2C, Y2D, Y2P, Y2S and Y2Z.

Y2B data format has been added.This format is used to sequence 2-digit, 1-bytebinary year data with CENTWIN processing.The binary values are converted todecimal, anhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad the two low-order digits are used as year data.Thus, while binary anddecimal values range from 00 to 255, year values range from 00 to 99.

Y2S data format has been added.Y2S is identical to Y2C and Y2Z for valid nu-meric data, but Y2S treats data beginning with X'00', X'40' or X'FF' as non-year data.Thus, the Y2S format can distinguish records, such as header/trailer records, thathave non-year data in the first byte of the year field, allowing such records to beprocessed differently from other records.

S treats non-year data as follows:Data with binary zeros (X'00') or a blank (X'40')in the first byte will not have century window processing applied to it.Instead, suchdata will be collated in sequence, before valid numeric year data for ascending orderor after the year data for descending order.Data with all binary ones (X'FF') in thefirst byte will also not have century window processing applied to it.Instead,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a suchdata will be collated after valid year numeric data for ascending order or before theyear data for descending order.

For applications that invoke SyncSort multiple times in an execution, you can now

multiple $ORTPARM DD statements to override SORT control statements gen-erated by the invoking program.This capability is particularly useful for COBOLprograms with multiple sort invocations involving century-sensitive date fields.SinceSyncSort's year data formats are not supported by COBOL, it is necessary to overrideSORT control statements generated by COBOL when a data format needs to bechanged for Year 2000 processing.For multiple sort executions in a single step, theoverride can now be accomplished with multiple $ORTPARM DD statements.

following describes Year 2000 capabilities provided with Release 3.7:

Year data fields for INREC/OUTREC can be used with editing.Year data fieldshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a for INREC/OUTREC can be used in arithmetic calculations.

Messages WER108I and WER110I now indicate CI SIZE for VSAM data sets and if

access was used.

of Changesxi

Message WER178A now indicates which DD in a SORTIN concatenation has a

-not-found condition.

Programmer'sGuide

1.Introduction

Introduction to SyncSort MVS

MVS is a high performance sort/merge/copy utility designed for use on IBMSystem 370 and 390 architectures and compatible computers.It executes under MVS/XA,MVS/ESA and OS/390 operating system environments.

is designed to conserve system resources, provide significant performance ben-efits and operate efficiently in both virtual and non-virtual environments.

can be initiated through job control language or invoked from a program writtenin COBOL, Phttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aL/1 or Assembler language. A JCL-initiated sort is more efficient becauseSyncSort totally controls the sort execution, including I/O management and main storagemanagement.Exit routines may be written in COBOL, C, FORTRAN, REXX or Assem-bler language to give a JCL sort additional programming flexibility. Exits may also be inPL/1 when SyncSort is invoked by a PL/1 program.

's Basic Functions

has three basic functions:

Sorting - rearranging data set records to produce a specific sequence.Merging - combining up to 100 pre-sequenced data sets into one data set which has

same sequence.

- reproducing a data set without going through the sorting process.

1. Introduction1.1

sort rearranges the records in a data set to produce a specific sequence, e.g., chrono-logical or alphabetic order. SyncSort provides four sortinghttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a techniques:

Disk Sort, the standard sorting http://www.wendangwang.comrmation in the Programmer's Guide

to the Disk Sort unless otherwise indicated.

, a maximum capacity sorting technique with an enhancedbreakpoint/restart capability.MAXSORT can sort any collection of data - regardlessof size - using a limited amount of disk space.MAXSORT is described in theMAXSORT chapter of this guide.

, a sorting technique that significantly reduces elapsed time for sortswhose input is a multi-volume tape data set and/or concatenated tape data sets.PARASORT improves performance by using multiple tape drives in parallel.PARASORT is described in the PARASORT chapter of this guide.

Sort, an alternative sorting technique used when intermediate storage must beassigned to tape.The Tape Sort is described in the Tape Sort chapter of this guide.

sort logically consists of four phhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aases which perform the following functions:

The control statements and JCL information are read and analyzed and the opera-

parameters for the sort are established.

input data is read into main storage and sorted.

necessary, intermediate results are written to temporary storage devices.

sorting process completes and the sorted data is written to the specified outputdevice(s).

merge combines up to 100 pre-sequenced data sets into one data set which has the samesequence.A merge has two phases which perform these functions:

The control statements and JCL information are read and analyzed and the opera-

parameters for the merge are established.

files are merged and the merged data is written to the specified output device(s).

copy reproduces a file, completely bypassing the sorting process.A copy hahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as two phaseswhich perform these functions:

The control statements and JCL information are read and analyzed and the opera-

parameters for the copy are established.

.2 Programmer'sGuide

The copied file is written to the specified output device(s).

's Data Utility and SortWriter Features

is designed to improve programmer productivity by reducing the time theprogrammer/analyst must spend designing, testing and debugging applications.WithSyncSort's extensive Data Utility and SortWriter features, data processing applicationspreviously requiring several steps can be accomplished in a single execution.

's Data Utility features include a multiple output facility, a full range of reportwriting capabilities, and record selection and record reformatting facilities.These optionsallow the user to design sort/merge/copy applications that can accomplishhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a a host of relatedtasks.

Multiple Output

multiple output facility (OUTFIL) allows multiple output files to be generated withjust one pass of the sort.Each of these files can have unique specifications that determinewhich records are to be included, how the records are to be formatted, and which reportcapabilities are to be used.Moreover, all these files can be written to the same outputdevice, or each can be written to a different device.

Reports

's SortWriter feature (OUTFIL) allows the user to design comprehensive reportseasily and efficiently.SortWriter options allow output data to beflexibly formatted withheaders and trailers, which can include data fields.Various kinds of numeric results canbe produced at report, page and section levels.These include totals, subtotals, minimums,subminimums, maximums, submaximums, averages, subaverages, record counts andsubcounts.Outpuhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at record fields can be realigned, the records can be padded with blanks,characters and binary zeros, and numeric data can be converted and edited.Automaticpagination, page numbering and dating are also provided.

Records, Reformatting Records and Summarizing Fields

selection, record reformatting and summing are other important SyncSort DataUtility features.Record selection via the INCLUDE/OMIT feature permits certain re-cords to be included or omitted from an input data set based on comparisons between twodata fields or between a data field and a constant.Date data formats work with theCENTWIN option to ensure that century evaluation is applied to INCLUDE/OMIT com-parisons involving 2-digit year data.

reformatting after input and/or before output, provided by the INREC/OUTRECcapability, allows the user to delete or repeat portions of records; insert spaces, charac-ters, binary zeros, and http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asequence numbers; realign fields; convert numeric data to itsprintable format; and convert data to its printable hexadecimal format.The CENTWINoption and date data formats enable conversion of 2-digit year fields to printable or

1. Introduction1.3

decimal 4-digit years of the appropriate century.The ability to delete irrelevantfields before sorting via INREC can provide important performance benefits. Additionally,the OUTREC facility can be used to convert a variable length record format input file intoa fixed length format output file.

SUM feature allows records with equal sort control fields to be deleted and optionallysummarizes numeric fields on those records.The deleted records can optionally be writ-ten to a separate data set.

SortWriter Report

report below illustrates the versatility of SyncSort's Data Utility and SortWriterfeatures.First, irrelevanthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a records are omitted from the input file and the input record isreformatted to eliminate unnecessary data fields.Then the file is sorted by invoice statusand invoice date. The output record is reformatted for readability and the numeric fieldsare converted and edited.The report itself is divided into sections and subsections basedon control field breaks.Headers and trailers identify the data fields, provide recordcounts and section and cumulative totals, and include the date and page number.

------------

NAME

------------

TRUST CO

----------- ADDRESS CO #----------- NYCNY 2681 CHIIL 2244 HOUTX 4762 WASDC 1177 STLMO 4633 CHIIL 2244 HOUTX 4762 BOS MA4986HOUTX 4762 ----- INV #----- 8601330686013298860132978601329http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a98602220086022198860221978512401185124016ACCOUNTS RECEIVABLE AGING REPORT FOR 01/30/92*********************************************INVOICESTATUS:O*****************--------INV DATE--------1/17/911/17/911/17/911/17/912/15/912/15/912/15/9112/15/9112/15/91---------------------INVOICEPRODUCTTAX---------------------1,100.0090.751,500.0075.002,500.00150.00650.0026.00550.0022.001,500.0075.00500.0030.001,500.0075.005,000.00300.00---------------------BALANCEPRODUCTTAX---------------------1,100.0090.751,500.0075.002,500.00150.00650.0026.00550.0022.001,500.0075.00500.0030.001,500.0075.005,000.00300.00PAGE:3DATE:04/22/92

NUMBER OF INVOICES:11 MONTHLY TOTALS:---------- ---------- ---------- ----------$22,850.00$1,484.50$22,850.00$1,484.50

---------- ---------- ---------- ----------

.00

,700.00

,750.00

.00

,600.00

.00

.00

.0029.2576.5070.0051.0064.0045.0http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a021.6036.00650.001,700.001,750.00850.001,600.00750.00360.00600.0029.2576.5070.0051.0064.0045.0021.6036.00BALTIC AVENUE CORPFASTEROOTEQUIPFEDERALFABRICSPATIOPRODUCTSTURENIUS FOR. EXCH.WINESASSOCIATESDESIGNTECHNOLOGIESPOLL DATA CORPCLE OHBALMD SHVLA MRYCA DTT MISMFCA LAXCA LAX CA06364980 5143 3029 83251794 2520 084686022207860222058602220486022203860222018602220985124017851240192/15/912/15/912/15/912/15/912/15/912/15/9112/15/9112/15/91

NUMBER OF INVOICES:8 MONTHLY TOTALS:---------- ---------- ---------- ----------$8,260.00$393.35$8,260.00$393.35

---------- ---------- ---------- ----------

.Sample SortWriter Report

.4 Programmer'sGuide

Environment Support

environment support allows you to choose an alternative set of sort collatingrules based on a specified national language.The alternative collating applies toSORT/MERGE and INCLUDE/OMIT processing.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aaremploys the callable services of IBM's Language Environment for MVS to collatedata in a way that conforms to the language and conventions of a selected locale.A localedefines single and multi-character collating rules for a cultural environment.Numerouspre-defined locales are available.

additional information, see “LOCALE” on page 5.21.

2000 Support

CENTWIN run-time and installation option and date data formats enable century-sensitive processing of date data involving 2-digit years.Century processing applies tosorting and merging, record selection and output data conversion.

's Operational Features

can take advantage of the expanded virtual storage available under MVS/XA,MVS/ESA and OS/390 without changes to JCL control streams. In addition, under ESA,SyncSort will take advantage of Data Space and Hiperspace to further improve perform-ance.SyncSort canhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a also interact with exits and invoking programs, including VS COBOLII, COBOL/370, C370 V2R1 with V2R2 C370 library, SAA AD/Cycle C370 Release 2 andIBM C/C   V3R2 programs.

's PARMEXIT feature permits the dynamic modification of PARM values basedon the conditions at execution time.This feature facilitates the passing of additionalparameters to specific jobs.

operational features include resident, reentrant code, interactive and streamlinedinstallation and maintenance procedures, automatic release or secondary allocation ofdirect access intermediate storage (SORTWK) and output (SORTOUT) space without JCLspecification, dynamic allocation of SORTWK space under MVS (DYNALLOC), and au-tomatic incore sorting.

's Value-Added Products

value-added products available from Syncsort can significantly improve sorting ef-ficiency.

SyncSort/COBOL Advantage is a fully automatic prodhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1auct which improves theperformance of COBOL programs that invoke SyncSort. The COBOL Advantage improves

1. Introduction1.5

time by 25 to 40% by enhancing processing of sequential files, including INPUTand OUTPUT procedure files.

SYNCSORT - An Accelerator for SAS&#174; Sorting is a high performance, trans-parent replacement for the SAS procedure PROC http://www.wendangwang.compared to PROC SORT,PROC SYNCSORT reduces the resources required for sorting within SAS applications,and cuts sort elapsed time.

enables SyncSort to run multiple sorts simultaneously on the same input data.For large input files, PipeSort significantly reduces total elapsed time compared to run-ning separate sort jobs.

more detailed information regarding each of these products, see “Chapter 14. Value-Added Products”.

of the Programmer's Guide

SyncSort MVS Prhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aogrammer's Guide is a reference manual designed for applicationsprogrammers who are using SyncSort to sort, merge or copy sequential data sets.Thismanual is self-contained and assumes only a basic working knowledge of the operatingsystem and its job control language.It should not be necessary to refer to any othermanual to produce an efficient sort.

Control Statements describes how to specify and use the SORT/MERGE,INCLUDE/OMIT, INREC/OUTREC, OUTFIL, RECORD, MODS, SUM, ALTSEQ andEND statements.The discussion of a particular control statement includes these topics:the statement's syntax format, the versatility provided by the various parameters, manyof which are unique to SyncSort, and the interaction between the control statement andother statements.

to Use SyncSort's Data Utility Features explains and illustrates the Data Utilityand SortWriter features through a series of sample applications.Each applicahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ation isself-contained and provides instructions for specifying both the required JCL and theappropriate control statements.

and Sample JCL/Control Statement Streams analyzes SyncSort's job controlrequirements and describes the SyncSort DD statements, each of which is illustrated withan example.JCL and control statement streams for MAXSORT and PARASORT are alsodescribed.Numerous examples are provided.

Options describes the operational parameters of SyncSort and identifies the de-livered defaults.This chapter explains how to specify such features as dynamic allocationof SORTWK space under MVS, automatic secondary allocation and release of SORTWKspace, the ability to skip a certain number of records or stop after sorting a certainnumber of records, and message routing.

SyncSort from a Program describes SyncSort invocation through assemblerprograms using 24-bit and 31-bit parameter lists.Numerous http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aexamples are provided.

.6 Programmer'sGuide

Coding and Use of Exit Programs indicates at which points during sort processinguser-written exit routines can be executed.Each exit point is fully documented togetherwith the appropriate tasks.Examples of COBOL E15 and E35 exit routines for fixed andvariable length records are included.

Flow of the Sort provides a skeletal view of the flow of control in the standard DiskSort (including the incore sort), merge and copy.This chapter indicates the order inwhich the control statements and exit routines are processed, information which is par-ticularly useful at the design stage of an application.

explains when MAXSORT should be used, describes its JCL requirements,control statements and PARM options, and provide examples.The chapter also examinesMAXSORT's restart capability and its operator interface.

explains the elapsehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad time advantages of the technique, the type of applica-tions where it can be applied, and the JCL requirements.

Sort describes the SyncSort DD statements needed for a tape sort and how toinititate a tape sort from JCL or a program.

Considerations describes how to design the most efficient application.It contrasts the merits of Disk Sort, PARASORT, MAXSORT and Tape Sort, JCL andinvoked sorts, the incore sort, and standard SORTWK techniques.Formulas for calcu-lating main storage and SORTWK requirements are provided.Other topics include theefficient use of control statements and PARMs, tuning main storage and SORTWK allo-cations and the use of the Checkpoint-Restart feature.

HISTOGRM Utility Program describes how to use the HISTOGRM program toreport on the composition of variable length files.This program indicates the averagerecord length, byte total, record total, block count and record couhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ant.Job control require-ments, control statements and messages are outlined.Sample job streams illustrate howto run HISTOGRM as a separate job and as an E15 exit during a variable length sort.Value-Added Products describes the SyncSort/COBOL Advantage, PROCSYNCSORT-An Accelerator for SAS&#174; Sorting and PipeSort.This chapter also providesdetailed information regarding their functions and special features.

documents all of the WERnnnx messages generated by the SyncSort program.This chapter includes sections describing &quot;Troubleshooting with WER999A UNSUC-CESSFUL SORT&quot; and &quot;What to Do before Calling SyncSort MVS Technical Services&quot;.

Reading

following guides supplement the information provided in the Programmer's Guide.Installation Guide

manual explains how to install and maintain SyncSort and defines the defaultoptions.

1. Introduction1.7

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

Guide.

handbook, intended for quick reference, provides the syntax for SyncSort controlstatements and briefly describes each parameter.

SyncSort: SortWriter Data Utilities Guide.

two-part user's guide demonstrates how SyncSort's versatile Data Utility featuresprovide an efficient, one-step alternative to writing, testing and debugging programs.Five comprehensive sample applications illustrate how the control statements work to-gether to produce formatted reports.

SyncSort: MAXSORT.

user's guide explains how to use the special MAXSORT feature of SyncSort to sortvery large amounts of data with only a limited amount of disk space.MAXSORT's uniquerestart capability is described and sample job control streams and tuning information areincluded.

Message Help

SyncSort messages and their explanations can be accessed online http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athrough anISPF/PDF dialog.Contact your system administrator for information about the operationof the message help facility.

.8 Programmer'sGuide

Chapter 2.SyncSort Control Statements

control statements tell SyncSort MVS how to process files.There are 12 controlstatements:

StatementFunction

an alternate collating sequence for control fields with an

format.

the end of control statements.

the criteria which determine whether or not records are

in an application.

the input record before sort/merge processing.

a merge or copy application and specifies merge control

.

user exit(s).

the criteria which determine whether or not records are

from an application.

the output file(s), and specifies SortWriter and http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aprocessing

.

the output record after sort/merge processing.

record information at various processing stages.ENDINCLUDEINRECMERGEMODSOMITOUTFILOUTRECRECORD

2. SyncSort Control Statements2.1

SORT

a sort or copy application and specifies sort control fields.Deletes records with equal control fields and summarizes numeric

on those records.

.2 Programmer'sGuide

Control Statement Summary Chart

following chart summarizes the parameters of each control statement and indicatesdefault values.Control

ALL  COND=   (comparisons)   [,FORMAT=f ]   NONE

=(field1[ ,field2]...)Sort/Merge all recordsParametersDelivered DefaultStandard EBCDICseriesCODE=(ccpp1 [,ccpp2]...)INRECInput records un-

FIELDS=(p1,l1,f1,o1 [http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,p2,l2,f2,o2]...)   FIELDS=(p1,l1,o1 [,p2,l2,o2]...) ,FORMAT=f   FIELDS=COPY

s   ,CENTWIN=  f

,CKPT   ,CHKPT

,EQUALS   ,NOEQUALS

[,FILES=n ]

[,SKIPREC=n ]

[,STOPAFT=n ]

,N exit-name1=(r1,b1 [, d1]   ,S    ,C     ,E     ,X     ,T               ),...,exit-name16=(...)    Copy all recordsCopy all recordsCentury windowstarts with currentyearNo checkpointNOEQUALSMODSNo exits

ALL  COND=   (comparisons)    [,FORMAT=f ]   NONE  Sort/Merge all records

2. SyncSort Control Statements2.3

Control

[FILES=(fileid1 [ ,fileid2]. . .)]

ddname   ,FNAMES=       (ddname1 [,ddname2] ...)

[,HEADER1=(field1 [,field2]. . .)]

[,HEADER2=(field1 [,field2]. . .)]

ALL      ,INCLUDE   =   (comparisons)      ,OMIT   NONE

n   ,LINES = ANSI     (ANSI,n)  ://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apar

[,NODETAIL]Delivered DefaultOne output fileOutput defined byFILESNo report headingNo page headingsOutput all records60 (if report-writingparameters)Detailed report

processing with

record

processing with

record

records not

for output

unchanged

format un-

split output

sections

report trailer

page trailers

format un-

record format

same as inputOUTFIL[,STARTREC][,ENDREC][,SAVE][OUTREC=(field1[,field2 ]...)][,CONVERT][,SPLIT][,SECTIONS=(field1 [ ,field2]...) ][,TRAILER1=(field1 [ ,field2]...) ][,TRAILER2=(field1 [ ,field2]...) ][FIELDS=(field1[ ,field2]...)]OUTREC[,CONVERT]

.4 Programmer'sGuide

Control

[TYPE=F|V]

[,LENGTH=(11,...,17)]

Fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aIELDS=(p1,l1,f1,o1 [p2,l2,f2,o2]...)   FIELDS=(p1,l1,o1 [p2,l2,o2]...) ,FORMAT=f   FIELDS=COPY

s   ,CENTWIN=  f

,CKPT   ,CHKPT  Delivered DefaultCentury windowstarts at current yearNo checkpoint

dynamic allocation

[,DYNALLOC=d/(d,n)/OFF] ,EQUALS   ,NOEQUALS

[,FILSZ=n ]

[,SIZE=n ]

[,SKIPREC=n ]

[,STOPAFT=n ]

FIELDS=(p1,l1,f1 [,p2,l2,f2]...)   FIELDS=(p1,l1 [,p2,l2]...) ,FORMAT=f   FIELDS=NONE

[,XSUM ]

.Control Statement Summary ChartSort or copy all re-cordsSort or copy all re-cordsNo summary of fields;no reduction of equal-keyed recordsSUM

Sort, MAXSORT, PARASORT and Tape Sort ControlStatement Requirements

following chart summarizes control statement usage for Disk Sort, MAXSORT,PARASORT and Tape Sort.

2. SyncSort Control Statements2.5

Control

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aQ

SortOptionalRequired if exits included

input streamMAXSORTand PARASORTOptionalRequired for MAXSORT ifexits included in input

; optional for

applicable

for exitsTape SortNot supportedRequired if exits includedin input streamINCLUDE/OMITINRECMERGEMODSOptionalOptionalRequired for merge orcopyRequired for exitsNot supportedNot supportedRequired for merge; copynot supportedRequired for exits; not

if program-

supportedOUTFILRequired for multiple out-

or reports

required

for sort or copy

; not applicable to

supported forMAXSORT;optional for PARASORTOptionalConditionally requiredRequired for sort; copy notsupportedOptionalOUTRECRECORDSORTSUMNot supportedConditionally requiredRequired for sorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a; copy notsupportedNot supported

.Control Statement Usage for Disk Sort, MAXSORT, PARASORT and Tape SortData Utility Processing Sequence

following chart presents the sequence in which SyncSort control statements and pa-rameters are processed.It includes those statements and parameters that modify theinput file (e.g., INCLUDE/OMIT), reposition record fields (e.g., INREC,OUTREC), andcreate reports (e.g., OUTFIL).

specifying record fields on any of these SyncSort control statements or parameters,refer to the record as it appears at that stage of SyncSort processing. For example, whenspecifying SORT fields be sure to take into account any repositioning of fields that maybe due to INREC processing.

.6 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

Figure2.Data Utility Processing Sequence

2. SyncSort Control Statements2.7

Control Statement Examples://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparexamples illustrating the syntax of each of the SyncSort MVS control statementsare included in this chapter.More complex applications are presented in “Chapter 3.How to Use SyncSort's Data Utility Features”.These applications demonstrate how theINCLUDE/OMIT, INREC, OUTREC, SUM and OUTFIL control statements can be usedto accomplish a variety of tasks, such as selecting input records, selecting input fields,combining records, reformatting output records, writing reports and creating multipleoutput.

for Control Statements

following rules apply to SyncSort MVS control statements.

Control Statements

Control statements can be in any order, except for the END statement which, ifspecified, must be last.

control statement, except for OUTFIL, can be specified only once for a particularapplication.

control statement can begin in column 2 through column 69.Ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1af labels are used,the control statement must be separated from the label by at least one blank.

control statement name must be the first field (or the first field after a label) ofthe first card image of the statement.It cannot be continued on a continuation cardimage.

last operand of each control statement must be followed by at least one blank.

Parameters

Parameters can take three forms:

ParameterParameter=value

=(value)

(value)

=(value1,value2,...,valuen)

(value1,value2,...,valuen);

that multiple values must be enclosed in parentheses.

Parameters can be in any order, but if parameters are present, the first parametermust begin on the first card image of a control statement.

.8 Programmer'sGuide

Parameters must be separated from each other by commas.Thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe parameter(s) must be preceded and followed by at least one blank.A blank

the parameter(s) from the control statement name and also indicates theend of the control statement.

the parameter(s) end in column 71, column 72 must contain a blank to signal theend of the control statement.

the exception of literal strings and constants, a parameter value cannot exceed28 alphanumeric characters.Parameter values cannot include commas, equal signsor parentheses.

the exception of literal strings specified as parameter values, blanks are notpermitted within parameters.

Field Positions, Lengths and Formats

Control statements reference fields by position p and length l.The first byte of every fixed length record is position 1, the second byte position 2,

so on.

1 through 4 of variable length records are reserved for the Record Descrhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aiptorWord (RDW).For these records, the first byte of the data portion is position 5.

control statements support bit-level processing. This means a binary controlfield can begin and end on any bit of any byte.The 8 bits in each byte are numbered0 through 7. For example, a position value of 7.4 designates a field beginning on thefifth bit of the seventh byte.A length value of 7.4 designates a field 7 bytes, 4 bitslong.

sure the position value takes into account any record reformatting and dataconversion that may have resulted from SyncSort data utility processing or exit pro-grams.Refer to the Data Utility Processing Sequence chart at the beginning of thischapter and to “Chapter 8.The Flow of the Sort”.

proper processing depends on data format, the format of the field must bespecified.

format of the field must be appropriate to the task.For example, only numericfields can be SUMmed.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparWhen all the fields have the same format, the format value can be specified just oncethrough the FORMAT=f subparameter.The FORMAT=f subparameter cannot beused when the INCLUDE/OMIT parameter is specified on the OUTFIL controlstatement.

2. SyncSort Control Statements2.9

Specifying Comments

Identify a comment card image by placing an asterisk (*) in column http://www.wendangwang.comments can

through column 80.

add a comment to a control statement card image, leave one or more blanks afterthe last parameter or comma on the image and follow with the comment, which canextend through column 71.

a comment that follows a control statement by coding an asterisk (*) incolumn 1 of the next card image or - if the control statement had ended - by placinga continuation character in column 72.

lines can be inserted between a control statement and its chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aontinuation bycoding an asterisk (*) in column one.

Continuation Card Images

statements cannot extend beyond column 71, but they can be continued.continue a control statement:

ToBreak after a parameter-comma or parameter-colon combination before column 72.

the continuation of the next card image anywhere between columns 2 and 71if there is no label on the continuation card.If there is a label, begin the continuationcard in any column from 3-71.No continuation character is required.

--or--

When the control statement extends through column 71 and cannot be broken at a

-comma or parameter-colon combination:

If the control statement does not contain a literal string that would extend be-

column 71, place a continuation character in column 72 and continue the

on the next card image anywhere between columns 2 and 7http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a1.

the control statement does contain a literal string that would extend beyond

71, place a continuation character in column 72 and begin the continua-

of the literal string in column 16 of the next card image.

following examples illustrate how card images can be continued.

.72SORTFIELDS=(1,10,A,20,5,A,45,7,A),FORMAT=CH,STOPAFT=100,EQUALS

.Continuing a Control Statement Without Specifying a Continuation

↓

.10 Programmer'sGuide

In the above example, no continuation character is required.The control statement isinterrupted after a parameter-comma combination before column 72.

.16COL.72OUTFIL OUTREC=(1:10,8,30:40,10),HEADER2=(1:'CUSTOMER NUMBXER',30:'ITEMNUMBER')↓↓

.Continuing a Control Statement with a Continuation Character

this example, a continuation character is necessary because the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aliteral string in theHEADER2 specification would extend beyond column 71.The 'X' in column 72 is thecontinuation character.The literal string is continued in column 16 of the next card im-age.

Labels

MVS supports labels.If labels are used, the following rules apply:

Labels are permitted on all SYSIN control statements, including continuation card

, but not on the control statements passed by an invoking program or the$ORTPARM DD statement.

must begin in column 1 with an alphabetic character.

can be any length, provided the other rules which apply to control statementsare followed.

least one blank must separate the label from the control statement name or pa-rameter that follows it.   Notational Conventions Used in the SyncSort MVS Programmer's Guide

Curly braces indicate that a choice must be made among the alternatives lishttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ated.Square brackets indicate an optional item.Two or more items in brackets are mu-

exclusive options; only one can be chosen for a particular application.

-case letters and numbers, commas, equal signs and parentheses must be en-tered exactly as indicated.Lower-case letters represent variables which must be re-placed by actual values.

show position in a series, and three dots indicate an ellipsis.

2. SyncSort Control Statements2.11

For example, a1,a2,...,a5. is equivalent to a1,a2,a3,a4,a5.and represents five a items(variables which will be replaced with actual values).

Examples which may be entered exactly as shown are presented in the Courier

, for instance: ALTSEQCODE=(F0B7,F1B8,F2B9,F3BA,F4BB,F5BC,F6BD,F7BE,F8BF,F9C0)

.12 Programmer'sGuideFigure 5.SampleExample

ALTSEQ

Control Statement

ALTSEQ http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acontrol statement constructs an alternate collating sequence for all controlfields for which the format code AQ has been specified on the SORT/MERGE statement,and/or an INCLUDE/OMIT statement, and/or an INCLUDE/OMIT parameter of theOUTFIL control statement.If an alternate collating sequence has been provided by in-stallation default, the AQ field(s) collate against this sequence, modified by the ALTSEQcontrol statement.If a default alternate sequence has not been provided, the AQ field(s)collate against the standard EBCDIC sequence, modified by the ALTSEQ statement. AQcan be specified for one or more control fields so that those control fields all use the samealternate collating sequence.

ALTSEQ statement cannot be specified for a Tape Sort.

Control Statement Format

format of the ALTSEQ statement is illustrated below:ALTSEQ CODE=(ccpp1 [,ccpp2]...)

.ALTSEQ Control Statement Format://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarParameter (Required)

CODE parameter specifies how the characters of the current collating sequence areto be reordered to create the alternate collating sequence.

CODE parameter can contain from 1 to 256 entries, each consisting of fourhexadecimal digits.These entries must be separated by commas and enclosed in paren-theses.

CODE entry consists of two parts:

cc value represents the character that is to be repositioned in the alternate

.

pp value indicates where the character represented by the cc value is tobe repositioned in the alternate sequence.pp

character represented by the cc value does not replace the character represented bythe pp value.If both characters occur as sort control fields, they will be considered equalin the collating process.

2. SyncSort Control Statements2.13

ALTSEQ

character (cc ehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1antry) can be moved only one time.However, more than one cc entrycan be mapped to the same pp value.

ALTSEQ Control Statements ALTSEQCODE=(F0B7,F1B8,F2B9,F3BA,F4BB,F5BC,F6BD,F7BE,F8BF,F9C0)

.Sample ALTSEQ Control Statement

sample ALTSEQ statement shows that the numbers 0 through 9 are to collate beforethe uppercase alphabet. ALTSEQCODE=(F040)

.Sample ALTSEQ Control Statement

sample ALTSEQ statement specifies that the number 0 is to collate as equal to ablank (X'40').

.14 Programmer'sGuide

END

Control Statement

present, the END control statement must be the last control statement.The ENDcontrol statement is required only when the control statements are not followed by /* orby a job control statement (i.e., when including exits in the input stream).

END statement has no parameters, but can contain comments if the commentshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a arepreceded by at least one blank.

2. SyncSort Control Statements2.15

INCLUDE/OMIT

/OMIT Control Statement

INCLUDE/OMIT control statement selects records from an input file based on com-parisons testing the contents of one or more fields within the record.A field can becompared to a constant or to another field within the record. Furthermore, a binary fieldmay enter into comparisons that involve testing the individual bits in the field.Only oneINCLUDE/OMIT control statement can be specified for an application, either as an IN-CLUDE or as an OMIT statement.

-Based Comparison Processing

supports alternative sets of collating rules based on a specified national lan-guage.The alternative collating applies to INCLUDE/OMIT (and OUTFILINCLUDE/OMIT) comparison processing as well as to SORT/MERGE processing.A lo-cale defines single and multi-character collating rhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aules for a cultural environment.

-based INCLUDE/OMIT processing applies only to character (CH) fields and char-acter or hexadecimal constants compared to character fields.When LOCALE is active,a CH to BI (or BI to CH) comparison is not allowed.The illegal comparison will causeSyncSort to terminate with an error message.

more information on locale-based processing, see “LOCALE” on page 5.21.

/OMIT Control Statement Format

format of the INCLUDE/OMIT statement follows.

.16 Programmer'sGuide

INCLUDE/OMIT   ALL   NONE      INCLUDE       ,AND,        COND= (c1    ,&amp;,  c2...  ) [ ,FORMAT=f ]   OMIT      ,OR,         , ,        c represents a comparison.Each comparison has this format:

,l1,

,EQ,   ,NE,     ,GT,    p2,l2[,f2]   [ ,f1]   ,GE,  constant   ,LT,   ,LE,      ,BO,          ,ALL,        ,BM,          ,SOME,        ,BZ,        http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a    ,NONE,        ,BNO,       ,BI       ,NOTALL,         ,BNM,          ,NOTSOME,        ,BNZ,          ,NOTNONE,      ,EQ,       bit pattern    ,NE,     ,EQ,   ,SS  constant   ,NE,

.                                                           bit mask                                INCLUDE/OMIT Control Statement Format

2. SyncSort Control Statements2.17

INCLUDE/OMIT

Parameter (Required)

COND parameter controls how records are included or omitted from an application.There are three forms of the COND parameter:

=ALL

=NONEAll of the input records are to be included.This is the default.None of the input records are to be included.

=comparison(s)Specifies one or more comparisons that determine which re-

are to be included or omitted.Two types of comparisons

possible:

A standard comparison, between two record fiehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1alds or

a record field and a constant.A binary input field

allows comparison by bit mask or bit pattern.

substring comparison, which allows the search for a

within a field or for a field value within a con-

://www.wendangwang.come SS as the format to indicate a substring com-

.

following several pages describe standard comparisons.For information on substringcomparisons, see “Substring Comparisons” on page 2.25.

field specified in the COND parameter is identified by its position (p), length (l) andformat (f).When processing variable length records, by default all fields specified mustbe contained within the record. If an application is expected to reference fields not com-pletely contained within the record, refer to “VLTESTI” on page 5.31.VLTESTI providesfor processing of records that do not contain all fields.

position http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1avalue indicates the first byte of the field relative to the

of the input record after E15 or E32 processing, if specified,

completed.The field must begin on a byte boundary.(Keep in

that if a variable length file is being referenced, the first 4 bytes

be reserved for the Record Descriptor Word.)

length value indicates the length of the field. The length must be

integer number of bytes. Refer to the table below for permissible

lengths by format.

format value indicates the format of the field. The permissible for-

for standard comparisons are indicated in the table below. If all

fields have the same format, the FORMAT=f subparameter can

specified instead of the individual f values. If both are specified, the

f values will be used.(Note that the f values must be speci-

for eachttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ah compare field).lf

.18 Programmer'sGuide

INCLUDE/OMIT

Format

/ OL

/ FS

/ LS

/ TS

/ OT

B

C/Y2Z

D

P

S

.Acceptable FieldLength (Bytes)1 to 2561 to 2561 to 2561 to 2561 to 2561 to 2561 to 2561 to 162 to 2562 to 2561 to 2561 to 2561 to 2562-8121221 to 256Valid Formats and Lengths of Include/Omit

definitions of the field format, see “Valid Formats for Merge Control Fields” on page

.33.

constant to which a field can be compared may be one of the following types:

2. SyncSort Control Statements2.19

INCLUDE/OMIT

decimal constant can be any length.It should not be enclosed in

quotes.It may or may not include a lehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aading   or - sign.For

, 100 is a valid decimal constant.The following numeric data

as equal:  0, -0, 0.

hexadecimal constant should be preceded by an X and specified in

of valid hexadecimal values which must be enclosed in single

: X'hh...hh'.For example, X'ACBF05' is a valid hexadecimal

.The sign of the field is implicit in the representation.

character constant should be preceded by a C and enclosed in single

: C'literal'.For example, C'SALES' is a valid character constant.

include an apostrophe in a character constant, specify it as two

; for example, C'D''AGOSTINO'.If a character constant

be continued on a second card image, place a continuation char-

in column 72 and then begin the continuation of the constant in

16 of the next card image.

are two mhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aethods in which the bit level characteristics of a binary input field canbe used to include or omit records.One is to compare the binary field to a bit mask; theother is to compare the binary field to a bit pattern.

bit mask is a string of bits, specified in terms of either hexadecimal

binary digits. The bit mask indicates which bits in the input field

to be tested. Each bit in the mask whose value is 1 (ON) is tested

the corresponding bit in the input field. If the value of a mask

is 0 (OFF), the corresponding bit in the input field is ignored.

hexadecimal format of a bit mask is X'hh...hh,' where each 'hh' re-

any pair of hexadecimal digits.

binary format of a bit mask is B'bbbbbbbb...bbbbbbbb', where each

'bbbbbbbb' represents 8 bits or a byte. Each bit is 1 or 0.The number

bits in a binary bit mask must be a mulhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atiple of 8.The maximum

of a binary bit mask is 256 bytes (2048 bits).

bit mask is truncated or padded on the right to the byte length of the

field. The pad character is X'00' or B'00000000'.

binary format of a bit pattern is B'bbbbbbbb...bbbbbbbb', where

'bbbbbbbb' represents 8 bits or a byte. Each bit is 1, 0, or period

(.).If the value of a bit in the bit pattern is 1 or 0, the corresponding

in the binary input field is compared to 1 or 0.If . (period) occurs

a bit position in the bit pattern, the corresponding bit in the input

is ignored.

number of bit positions in a bit pattern must be a multiple of 8.

maximum length of a bit pattern is 256 bytes (2048 bits).hexadecimalcharacter

.20 Programmer'sGuide

INCLUDE/OMIT

bit pattern is truncated or padded rightward to the byte lehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1angth of the

input field. The pad character is B'00000000'.

comparison operators represent the following conditions:

(or ALL)

(SOME)

(NONE)

(NOTALL)EqualtoNot equal toGreaterthanGreater than or equal toLessthanLess than or equal toAll mask bits are 1s (ON) in the input fieldSome but not all mask bits are 1s (ON) in the input fieldNone of the mask bits is 1 (ON) in the input fieldSome or no mask bits are 1s (ON) in the input field

(NOTSOME)All or no mask bits are 1s (ON) in the input field

(NOTNONE)All or some mask bits are 1s (ON) in the input field

for Multiple Comparisons

comparisons are separated by ANDs or ORs to form a logical expression.(Al-ternatively, &amp; and | may be used for AND and OR).When evaluating an expression, eachcomparison cn is evaluatedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a first.Then, AND conditions are evaluated before OR condi-tions.

may be used around groups of comparisons to change the default evaluationorder.Any number of nested parentheses may be used.Conditions within parenthesesare evaluated first, from innermost to outermost parentheses.

example, if you wanted to select all records from your Paris office for 1995 and 1996,you might incorrectly specify:

COND=(1,4,CH,EQ,C'1995',OR,1,4,CH,EQ,C'1996',

,5,5,CH,EQ,C'PARIS')

AND operator in the above statement would be evaluated first, producing unexpectedoutput.The correct statement would be:

COND=((1,4,CH,EQ,C'1995',OR,1,4,CH,EQ,C'1996'),

2. SyncSort Control Statements2.21

INCLUDE/OMIT

,5,5,CH,EQ,C'PARIS')

added parentheses force the OR operator to be evaluated first, thus producing theexpected output.

Fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aield-to-Field Standard Comparisons for Non-date Fields

format of a data field determines whether or not it can be compared to another datafield.The figure below illustrates which field-to-field comparisons are permitted.

ZDXXXXXXXXXXXXXXXXXXXXXXXXXXXX

.Permissible Field-to-Field Comparisons for Non-year Data FormatsSpecifying Field-to-Field Standard Comparisons for Year Fields

year data formats that can be used with INCLUDE/OMIT are Y2B, Y2C, Y2D, Y2P,Y2S and Y2Z.Year data formats can only be compared to other year formats; they cannotbe compared to formats in the table above.

year data formats work with the CENTWIN run-time parahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ameter or installation op-tion to define a 2-digit year value that is to be treated as a 4-digit year.CENTWIN de-

.22 Programmer'sGuide

INCLUDE/OMIT

a sliding or fixed 100-year window that determines the century to which 2-digit yeardata belongs when processed by INCLUDE/OMIT and other control statements.

year data formats and CENTWIN ensure that century evaluation is applied toINCLUDE/OMIT comparison conditions involving 2-digit year data.For example, with-out CENTWIN processing, an INCLUDE/OMIT comparison would treat the year 01 as&quot;less than&quot; the year 98.With CENTWIN processing, the 01 field could be recognized asa twenty-first century date (2001), which would be treated as &quot;greater than&quot; 98 (1998).For details on the CENTWIN option, see “CENTWIN” on page 5.8.For details on the yeardata formats, see “CENTWIN Parameter (Optional)” on page 2.111.For an example IN-CLUDE stathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aement with a condition involving a year data field, see Figure16 on page

.29.

following table summarizes the valid field-to-field comparisons for year data formats:

B

B

C/Y2Z

D

P

S

.XY2C/Y2ZY2DY2PY2SXXXXXXXXXX Permissible Field-to-Field Comparisons for Date

FormatsPadding of Compared Fields

two fields are compared, the shorter field is padded to the length of the longer field.Padding takes place as follows:

The padding characters are blanks when the shorter field is in character format;

, they are zeros of the shorter field's own format.

is on the right if the shorter field is in BI, CH or PD0 formats.Padding ison the left for all other formats.

2. SyncSort Control Statements2.23

INCLUDE/OMIT

Field-to-Constant Standard Comparisons

fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aormat of a data field determines the type of constant to which it can be compared.The figure below illustrates which field-to-constant comparisons are permitted.Format

/ OL

/ FS

/ LS

/ TS

/ OT

B

C/Y2Z

D

P

S

(bit pattern)XXXXXXXXXXXXXXXXXX

.Permissible Field-to-Constant ComparisonsXXX

constant will be padded or truncated to the length of the field with which it is compared.Decimal constants are padded or truncated on the left; hexadecimal, binary and characterconstants are padded on the right. The padding characters are:

stringB'00000000'

.24 Programmer'sGuide

INCLUDE/OMIT

string

string

'40http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a'X'00'Zeros of proper format. Decimal constants for all Y2 formats are

or truncated to two decimal digits representing a year.

year constant will then have CENTWIN processing applied

it for comparison to a Y2 field. The constants for PD0 com-

should not include the first digit and trailing sign of the

data that will be ignored.Thus, a PD0 field of n bytes will

compared to a constant of n-1 bytes.

Comparisons

comparison (SS format) can be based on either of the following searches:

Match occurrence of a constant within a record fieldMatch occurrence of a record field within a constant.

the first form, the length of the constant is less than the length of a specified field.Records will be searched for the occurrence of the constant anywhere within the field.The condition will be true if an EQ operator is specifiehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad and the constant is found or if aNE operator was specified and the constant is not found.For example, consider theconstant &quot;ANYTOWN&quot; and a 60-byte field that contains an address.Records will besearched for the occurrence of the literal &quot;ANYTOWN&quot; anywhere within the 60-byte ad-dress field.If a match is found and the logical operator is EQ, then the logical result is&quot;true.&quot;The logical result is also &quot;true&quot; if the literal does not appear within the 60 bytesand the logical operator is NE.

the second form, the length of a constant is greater than the length of a specified field.Records will be searched for an occurrence of the field within the constant.For example,the constant 'A02,A05,A06,A09', which is composed of substrings separated by commas,can be compared against the contents of a 3-byte field within the record.If the 3-bytefield matches any 3-byte character string in the constahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ant, the logical result is &quot;true&quot; if thelogical operator is EQ.

character used to separate elements of the constant should be a character that doesnot appear in the field being compared.The comparison is then equivalent to a standardcomparison with ORed conditions.That is, the condition is true if 'A02' OR 'A05' OR 'A06'OR 'A09' is found in the field being compared.The substring comparison is a much morecompact expression than multiple OR conditions in a standard comparison.

both forms of substring comparison, constants and fields in the record can be from 1to 256 bytes in length.Constants can be in either character or hexadecimal format.(Refer to the description of constants just after Table6 on page 2.24.)

Figure15 on page 2.28 for an example of how to use the substring comparison.

2. SyncSort Control Statements2.25

INCLUDE/OMIT

INCLUDE/OMIT Control Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atatements

1 INCLUDECOND=(24,4,PD,LT,28,4,PD,OR,10,2,CH,EQ,C'NY')

.Sample INCLUDE Control Statement

this example, records will be included in the application if the numeric data in the fieldbeginning in byte 24 is less than the numeric data in the field beginning in byte 28 or ifthe character data in the field beginning in byte 10 is equal to NY.

2 OMITCOND=(1,3,ZD,EQ,100,AND,20,1,CH,NE,X'40')

.Sample OMIT Control Statement

this example, records will be omitted from the application if the numeric data in thefield beginning in byte 1 is equal to 100 and if the character data in byte 20 is not equalto a blank (X'40').

next set of control statements exemplifies record selection using bit level logic. Thefirst two examples involve a comparison between a bit mask (shown coded in binary andhexadecimal format) and a binary input field. The third examhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aple is a comparison betweena bit pattern and a binary field.

3 INCLUDECOND=(10,1,BI,ALL,B'01001000')

INCLUDE COND=(10,1,BI,ALL,X'48')

.Sample INCLUDE Control Statement Using a Bit Mask

record selection condition has the following elements (from left to right): a binaryfield (BI) of length 1 byte that starts at column 10 of the record, a comparison operator(ALL), and a bit mask (B'01001000' in binary, X'48' in hexadecimal).Counting from the

.26 Programmer'sGuide

INCLUDE/OMIT

, the second and fifth bits of the bit mask are ON (1). For the selection condition tobe true, the same bits must be ON in the binary input field. Therefore, if the input fieldcontains, for example, 01001000, 01111000 or 11111111, the condition for the inclusionof records is satisfied. However, if the input field contains a bit string where both maskbits are not ON (e.g., 01000000, inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a which the fifth bit is not ON), the condition fails andthe records are omitted.

4 INCLUDECOND=(10,1,BI,NOTNONE,B'01001000')

INCLUDE COND=(10,1,BI,NOTNONE,X'48')

.Sample INCLUDE Control Statement Using a Bit Mask

condition for the inclusion of records is met if at least one of the mask bits is ON inthe input field. Therefore, the condition would evaluate as true, if the bit string in thebinary field were 01000000 (the second bit is ON), 000010000 (the fifth bit is ON),01001000 (both the second and fifth bit are ON). However, with the string 10000111, forinstance, in the input field, the specified condition would evaluate as false (resulting inthe omission of records), since neither mask bit is ON.

above method of comparing a binary input field to a bit mask is useful for testing thecontents of a &quot;flag&quot; byte where each bit has a different meaning.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a 5.

COND=(21,4,BI,EQ,B'000000010001........100100011111')

.Sample INCLUDE Control Statement Using a Bit Pattern

condition specifies a 4-byte long binary input field (BI) in column 21, a logical re-lationship (EQ), and a bit pattern.The bit pattern describes the required sequence of 1sand 0s in the first and last twelve bit positions.The row of periods in the pattern re-presents the part of the string that is irrelevant to the definition of the condition.Thecondition is true, if the sequence of 1s and 0s in the input field is identical to that de-scribed in the bit pattern.

method of comparing a binary input field to a bit pattern is useful when testing fornumeric digits that are one half byte each, as in the packed data format. For example,assume that the binary input field specified in the condition above is a date field in thePD format X'0mmddyyF'.Each date element is split acrohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ass a byte boundary. The secondhalf-byte of each byte (except the last) represents the first of the two digits that form a

2. SyncSort Control Statements2.27

INCLUDE/OMIT

element (mm,dd,yy). (In the last byte, the second half-byte--1111 in binary and F inhexadecimal--stands for the fact that the bit pattern encodes a packed decimal.) The firsthalf-byte of each byte (except the first) represents the second digit of a date element(mm,dd,yy).(The first half-byte, i.e. 0000, of the bit pattern gives it the length specifiedfor the binary field at column 21.)Mapping this scheme onto the bit pattern in the control

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

[此处图片未下载成功]

statement results in the following.

is, the above control statement is an instruction to select just those records in whosedate field mm and yy equal 11 and 91, respectively, while dd can have any value. In otherwords, the records thus selected are those from November 1991.

6

following example illustrates substring comparisons.INCLUDE COND=(11,60,EQ,C'ANYTOWN',

,121,3,EQ,C'A01,A05,A06,A09'),FORMAT=SS

.Sample INCLUDE Control Statement Using Substring Compares

this example, a record will be included in the application if either of the followingconditions is true:

The literal 'ANYTOWN' is found in the 60-byte field starting at position 11 in the

.

contents of the 3-byte field starting at position 121 matches one of the four sub-strings ('A02', 'A05', 'A06', or 'A09') in the constant.

7

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparThe following example illustrates an INCLUDE comparison based on CENTWIN proc-essing.

.28 Programmer'sGuide

INCLUDE/OMIT INCLUDE COND=(20,2,Y2C,GT,96)

.Sample INCLUDE Control Statement with CENTWIN Processing

this example only records whose data is from the years greater than 1996 will be in-cluded in the application. If the CENTWIN parameter were set to 1980, representing acentury window of 1980 to 2079, the records would be processed in the following manner: Contentsof

20 and 21

RecordDispositionOmitted- represents 1984Included - represents 1999Included - represents 2037

using the INCLUDE/OMIT control statement are illustrated in “Chapter 3.How to Use SyncSort's Data Utility Features”.

2. SyncSort Control Statements2.29

INREC

Control Statement

INREC control statement reformahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ats the input http://www.wendangwang.come the INREC statement toadd, delete or reformat fields before the records are sorted or http://www.wendangwang.come the OUTRECstatement or the OUTREC parameter of the OUTFIL statement to delete or reformatfields after the records are sorted or merged.Note that INREC is performed after E15exit processing and INCLUDE/OMIT control statement processing.

the INREC control statement to delete data fields improves sort performance byreducing the number of bytes SyncSort MVS must process.The same result may beachieved in some cases by changing the data format of certain fields.For example, if youneed to change the format of a ZD field to PD, which reduces the number of bytes for thefield, it is more efficient to use INREC rather than OUTREC for the converson.Addi-tionally, for SORT/MERGE processing PD fields are processed more efficiently than ZDfields.

for CONVERT, all the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afunctions performed by the OUTREC statement, such asinserting character strings or changing the data format of a numeric field, can also beperformed by the INREC statement.(See “OUTREC Control Statement” on page 2.74 foran explanation of these functions.)For example, you can use the INREC statement toinsert zeros of the proper format to expand a numeric field before SUM processing toprevent arithmetic overflow.However, you will usually want to use the OUTREC state-ment rather than the INREC statement to expand the record because OUTREC process-ing takes place after records are sorted or merged.

you use the INREC statement to reformat the input record, remember to use thepost-INREC field positions when you specify the SORT, MERGE, SUM, OUTREC and/orOUTFIL statements.

the SEQNUM function is used in a SORT application to insert a sequence number fieldin the record, this field will reflect the order of the records phttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arior to sorting.In a MERGEapplication, the field will reflect the order of the records as they were read from each in-put in the merge.

Control Statement Format

format of the INREC statement is illustrated below:INREC FIELDS=(...)

.INREC Control Statement Format

.30 Programmer'sGuide

INREC

Parameter (Required)

FIELDS parameter specifies the data fields to be included in the application.See“OUTREC Control Statement” on page 2.74 for a complete description of the FIELDSparameter.

INREC Control StatementINREC FIELDS=(1:1,20,21:40,15,ZD,PD,29:60,5)

.Sample INREC Control Statement

INREC statement specifies three data fields from an 80-byte record:

The first field begins in byte 1 of the input record and is 20 bytes long.The second field begins in byte 40 of the input record and is a 15-byte ZD field.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aThe

format is to be converted to PD.Since the input field contains 15 decimal digits,the converted PD output field created by SyncSort will be 8 bytes long.

third field begins in byte 60 of the input record and is 5 bytes long.

three fields have been positioned to begin in bytes 1, 21, and 29, as indicated bytheir column prefixes.

reformatted input record is now just 33 bytes long.

comprehensive examples that illustrate the INREC control statement see “Chapter

.How to Use SyncSort's Data Utility Features”.

2. SyncSort Control Statements2.31

MERGE

Control Statement

MERGE control statement is required for every merge application.The MERGEstatement can also define a copy application.

Environment Support

environment support allows you to choose an alternative set of collating rulesbased on ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a specified national language.The alternative collating applies toSORT/MERGE and INCLUDE/OMIT processing.

additional detail, see “LOCALE” on page 5.21.

Control Statement Format

format of the MERGE control statement is illustrated below:  FIELDS=(p1,l1,f1,o1 [,p2,l2,f2,o2] ...)MERGE   FIELDS=(p1,l1,o1 [,p2,l2,o2] ...),FORMAT=f  FIELDS=COPY

,CENTWIN =       ,CKPT    ,EQUALS   [,FILES=n ]   f      ,CHKPT     [ ,SKIPREC=n ] [ ,STOPAFT=n ]

.MERGE Control Statement Format

Parameter (Required for a Merge)

FIELDS parameter is required for a merge.It describes the control fields.

the control fields in order of greatest to least priority, with the primary control fieldlisted first, followed by progressively less significant fields.You can specify up to 128control fields; however, if fields require complex internal processing, the limit for ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a par-ticular execution may be less than 128.

field specified in the FIELDS parameter is identified by its position p, length l,format f and order o.

position value indicates the first byte of the field relative to the beginning

the input record after INREC and/or E32 processing, if specified, have com-pleted.

.32 Programmer'sGuide

MERGE

control fields can begin on any bit of a byte.When a binary field doesnot begin on a byte boundary, you must specify the bit number (0-7).For ex-ample, a position value of 21.3 refers to the 4th bit of the 21st byte of the re-cord.

length value indicates the length of the control field.The length value

be an integer number of bytes, except for the length of a binary controlfield which can be specified in bits.For example, a length value of 0.5 refersto a binary control field 5 bits long.

signed fieldshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a, the length value must include the area occupied by the sign.fThe format value indicates the data format.For a list of valid formats, refer

the Format Code Chart in the next section, &quot;Valid Formats for Merge Con-trol Fields.&quot;If all the control fields have the same format, you can specifytheformat value once by using the FORMAT=f subparameter.If you specify boththe individual f values and the FORMAT subparameter, the individual f valueswill be used.(Note that the f values must be specified for each control field).The order value indicates how the field is to be collated:

=AscendingorderD=Descendingorder

=As modified by an E61 exit.o

Formats for Merge Control Fields

following table lists the valid formats for merge control fields.Code

*

*Data FormatEBCDIC characters are translated to their ASCII equivalents beforesorting.Character. Records are sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ated according to an alternate sequence

either in the ALTSEQ control statement or as an installation

.

separate sign. An ASCII   or - precedes numeric field.One

per byte.

separate sign. An ASCII   or - trails numeric field.One digit

byte.

. Unsigned.

. Unsigned.Field Length(bytes)1 to 2561 to 256ASL*AST*BICH2 to 2562 to 2561 bit to 4092**1 to 4092**

2. SyncSort Control Statements2.33

MERGE CLO*

*Leading overpunch sign. Hexadecimal F,C,E, or A in the first 4 bitsof your field indicates a positive number. Hexadecimal D or B in the

4 bits indicates a negative number. One digit per byte.

=CLC is forced.

sign format.An optional leading sign may be specified im-

to the left of the digits.If the sign is a -, the number is

ashttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a negative.For other characters, the number is treated as

.Characters to the left of the sign are ignored.

separate sign. An EBCDIC   or - precedes numeric field.

digit per byte. CMP=CLC is forced.

separate sign. An EBCDIC   or - follows numeric field.One

per byte. CMP=CLC is forced.

point. Signed. (Equivalent to Signed Binary.)

point. Normalized. Signed.

decimal. Signed.

decimal.2-8-byte packed decimal data with the first digit and

sign ignored.The remaining bytes are treated as packed

digits.Typically PD0 is used with century window processing

Y2P format; Y2P processes the year, while PD0 processes month

day.

. 2-digit, 1-byte binary year data treated as a 4-digit year by

(century window) processing.

.2-digit chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aharacter year data treated as a 4-digit year by

(century window) processing.Processing is identical to

Z fields.

decimal.2-digit, 1-byte packed decimal year data treated as

4-digit year by CENTWIN (century window) processing.

decimal.2-digit, 2-byte packed decimal year data.Of the four

digits contained in the 2 bytes, the first digit and trailing sign

ignored; the two inner digits are treated as a 4-digit year by

processing.1 to 256CSFFS1 to 16CSL*LS*CST*TS*FIFLPDPD0*2 to 2562 to 2561 to 2562 to 161 to 2562-8Y2B*Y2C*12Y2D*Y2P*12

.34 Programmer'sGuide

MERGE

S*Character or zoned decimal.2-digit, 2-byte valid numeric data

as a 4-digit year by CENTWIN (century window) processing,

for Y2C and Y2Z.However, certain data is not treated as year

.Data with binary zeros (X'00') or ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a blank (X'40') in the first byte

be collated before valid numeric year data for ascending order

(after year data for descending order).Data with all binary ones

(X'FF') in the first byte will be collated after valid numeric year data

ascending order (before year data for descending order).Zones are

, as for Y2C and Y2Z, except for data where the first byte be-

with X'00', X'40' or X'FF'.

decimal.2-digit, 2-byte zoned decimal year data treated as a

-digit year by CENTWIN (century window) processing.The zones

ignored.Processing is identical to Y2C fields.

decimal. Trailing overpunch in the first 4 bits of the rightmost

gives the sign. Hexadecimal F,C,E, or A indicates a positive

. Hexadecimal D or B indicates a negative number. One digit

byte. CTO forces CMP=CLC.

* Cannot be used with http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aTape Sort.

** 4084 for variable-length records.

.Format Code Chart2Y2Z*2ZDCTO*OT*Note:1 to 256

information on the year data formats (Y2B, Y2C, Y2D, Y2P, Y2S and Y2Z) plus therelated data format PD0, see “CENTWIN Parameter (Optional)” on page 2.36 and “Con-verting Year Data with Century Window Processing on INREC, OUTREC or OUTFILOUTREC” on page 2.84.Also see &quot;Specifying Field-to-Field Standard Comparisons forYear Fields&quot; in the INCLUDE/OMIT Control Statement section of this chapter.

for Specifying Control Fields

For fixed length records, the sum of the lengths of all control fields cannot exceed

bytes.When EQUALS is in effect, the sum of their lengths cannot exceed 4088bytes.

variable length records, all control fields must be located within the first 4084bytes and the sum of their lengths cannot exceed 4084 bytes.When EQUALS is ineffect, all contrhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aol fields must be located within the first 4080 bytes and the sum oftheir lengths cannot exceed 4080 bytes.

fields can be in contiguous or noncontiguous locations in the record.

that for variable length records, the first 4 bytes are reserved for the Re-cord Descriptor Word, so the first byte of the data portion of the record is byte 5.

2. SyncSort Control Statements2.35

MERGE

If the output file is a key-sequenced VSAM cluster, the VSAM key must be the first

field specified.

PD and ZD Control Fields

CMP PARM determines how PD and ZD control fields will be compared.WhenCMP=CPD is in effect, the Compare Decimal (CP) instruction is used for the compare.ZD fields are packed and then compared.This method has performance advantages.However, invalid PD data may cause a system 0C7 abend and program termination.Moreover, the integrithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay of ZD fields is only guaranteed when they contain valid ZD data.The CMP=CPD method cannot be used for control fields that exceed 16 bytes, for variablelength merges when an even value (0, 2, 4 or 6) is specified for the VLTEST PARM, or fora Tape Sort.

CMP=CLC is in effect, no data validation is performed and the integrity of theoutput is maintained, even if the sign for a PD or ZD field is invalid.This method is al-ways used if any control field exceeds 16 bytes, for variable length merges when an evenvalue is specified for the VLTEST PARM, and for a Tape Sort.

Parameter (Optional)

CENTWIN run-time or installation option acts on 2-digit year data.At run-time,CENTWIN can be specified as either a PARM option or a SORT/MERGE statement pa-rameter.CENTWIN generates a century window (for example, 1950 through 2049) thatdetermines the century to which a 2-digit year belongs.CENTWIN ensures that yearhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adata spanning centuries will be sequenced correctly.Without CENTWIN processing, anascending collation would sequence the year 01 before the year 98.With CENTWINprocessing, the 01 field could be recognized as a twenty-first century date (2001) andwould thus be sequenced after 98 (1998).

more information on specifying the CENTWIN option, see “CENTWIN” on page 5.8.CENTWIN processing only applies to data defined as year data formats:Y2B, Y2C, Y2D,Y2P, Y2S, and Y2Z.These data formats enable SyncSort to process 2-digit year fields as4-digit years.A related data format, PD0, can be used to process the month and dayportions of packed decimal date fields.To correctly specify date fields for CENTWINMERGE processing, you should be familiar with the CENTWIN-related data formats.The following describes each of the year data formats and provides MERGE controlstatement examples:

Y2B Format

format is used to sequehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ance 2-digit, 1-byte binary year data with CENTWIN proc-essing.The binary values are converted to decimal, and the two low order digits are usedas year data.Thus, while binary and decimal values range from 00 to 255, year values

.36 Programmer'sGuide

MERGE

from 00 to 99.The relationship between binary, decimal and year values is shownin the following table:

Value

'00' to X'63'

'64' to X'C7'

'C8' to X'FF'Decimal Value00 to99100 to 199200 to 255Year Value00-9900-9900-55Table8. Possible Values Representing Year Data

Y2BThe Y2C and Y2Z Formats

formats represent 2-digit, 2-byte year data in either character (Y2C) or zoned dec-imal (Y2Z) format.Either Y2C and Y2Z formats can be used with data of the formX'xyxy'

y is a hexadecimal year digit 0-9 and x is hexadecimal 0 through F.Y2C and Y2Zignore the x digits, leaving yy, the 2-digit unhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asigned year representation.

you have a character or zoned decimal date field mmddyy that begins at byte 20.You can use either Y2C or Y2Z to process the yy field.As the following example indicates,you could specify three sort keys to correctly sort this date:

FIELDS=(24,2,Y2C,A,

,2,CH,A,

,2,CH,A)* Collates yy field as 4-digit year* Collates mm field* Collates dd field

yy field (24,2) will be processed according to the century window setting.For exam-ple, if CENTWIN=1945, the field yy=45 will be sequenced as if it were 1945, and yy=44would be sequenced as if it were 2044.Thus, for an ascending sort, 44 would follow 45.The Y2D Format

format is used to sequence 2-digit, 1-byte packed decimal year data with http://www.wendangwang.come Y2D to extract the year data yy from packed decimal date fields.Forexample, consider a 3-byte packed decimal data field defined as

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarChapter 2. SyncSort Control Statements2.37

MERGE

'yyddds'

field has the year yy in the first byte and the day ddd in bytes 2 and 3.The packeddecimal sign s would be in the last digit (half byte) of the third byte.To sort this datefield, which begins at byte 20, with 4-digit year processing, use the following MERGEcontrol statement:MERGE FIELDS=(20,1,Y2D,A,

,2,PD,A)* Collates 2-digit year as 4-digit year* Collates ddds as 3 digits (ddd)

Y2P Format

format is used to sequence 2-digit, 2-byte packed decimal year data with http://www.wendangwang.come Y2P to extract the year data yy from packed decimal date fields spanning2 bytes.For example, a packed decimal date of the form yymmdd would be stored as 4bytes:

= X'0yymmddC'

the trailing C (sometimes F) is a positive sign and the leading 0 pads the field onthe left to make an even number of digits.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arthat the components of the date span bytes:

y ym md dC

P handles this condition by ignoring the first and last half bytes of the 2-byte fieldspecification.Thus, Y2P processes 0yym as yy, ignoring the leading digit (0) and thetrailing digit m that is part of the month.The following example uses Y2P to collate the year portion of the date field, which beginsat byte 20:

FIELDS=(20,2,Y2P,A) * Collates yy field as 4-digit year

field specification 20,2,Y2P treats X'0yym' as X'yy', and CENTWIN processing sortsyy as a 4-digit year yyyy.

PD0 format, described below, can assist Y2P by processing month and day data thatoverlaps year data in the original field.

.38 Programmer'sGuide

MERGE

Y2S Format

format is used to sequence 2-digit, 2-byte character or zoned decimal data.The Y2Sformat is identical to Y2C and Y2Z for valid numeric data, buthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Y2S treats data that beginswith X'00', X'40' or X'FF' as non-year data.Thus, the Y2S format can distinguish recordsthat have non-year data in the first byte of the year field, allowing such records to becollated differently from other records.

S treats non-year data as follows:

Data with binary zeros (X'00') or a blank (X'40') in the first byte will not have century

processing applied to it.Instead, such data will be collated in sequence, be-fore valid numeric year data for ascending order or after the year data for de-scending order.

with all binary ones (X'FF') in the first byte will also not have century windowprocessing applied to it.Instead, such data will be collated after valid year numericdata for ascending order or before the year data for descending order.

are ignored, as for Y2C and Y2Z, except for data where the first byte begins withX'00', X'40' or X'FF'.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arAs an example, suppose you want to preserve the input order of header and trailer recordsat the start or end of the file, and your header/trailer records are identified by binaryzeros (X'00'), a blank (X'40') or binary ones (X'FF') in the first byte of the date field.TheY2S format allows CENTWIN to identify the header/trailer records and treat them dif-ferently from other records.

PD0 Format

format is used to sequence 2-8 byte packed decimal data.PD0 ignores the first digitand trailing sign during processing.PD0 is normally used in conjunction with the Y2Pdata format.The Y2P format is used to process the 2-digit year portion of a packed dec-imal date field, while the PD0 format is used to process the month and day portion of thefield.

PD0 is typically used with Y2P, CENTWIN processing is not applied to PD0.Consider the packed decimal date field used in the Y2P example above:

= Xhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a'0yymmddC'

the trailing C (sometimes F) is a positive sign and the leading 0 pads the field onthe left to make an even number of digits.

that the components of the date span bytes:

y ym md dC

2. SyncSort Control Statements2.39

MERGE

date can be processed as follows:

Y2P processes the year component X'0yym' as X'yy'.PD0 processes the month and day components X'ymmddC' as X'mmdd'.

following MERGE control statement can be used to collate the entire date withCENTWIN processing:MERGE FIELDS=(20,2,Y2P,A, * Treats X'0yym' as X'yy'; collates yy as yyyy

,3,PD0,A) * Treats X'ymmddC' as X'mmdd'

=COPY (Required for a Copy)

FIELDS=COPY to copy one or more input files.(Multiple files can be copied if theyare concatenated on the SORTIN DD specification.)Other control statements such asINCLUDE/OMIT, INREC, OUTREC and Ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aUTFIL may be specified in conjunction witha copy application, allowing you to edit and reformat the file(s) without any collationprocessing

SUM control statement and an E32 exit cannot be specified with FIELDS=COPY.All Phase 3 exits can be used.

SORTIN DD statement defines the input to be copied.(SORTINnn DD statementsare not processed when FIELDS=COPY is specified.)

/CHKPT Parameter (Optional)

CKPT/CHKPT parameter instructs SyncSort to take a checkpoint at every end-of-volume of a SORTOUT data set when OUTFIL is not used.Either spelling is accepted.This parameter requires a SORTCKPT DD statement.It cannot be specified in conjunc-tion with a user-issued STIMER macro or an incore sort.Checkpoints cannot be takenwithin a user exit routine.

to “Chapter 12. Performance Considerations” for an explanation of theCheckpoint/Restart feature.

.40 Programmer'sGuide

MERGhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aE

/NOEQUALS Parameter (Optional)

EQUALS parameter insures that equal-keyed records are merged in the order of theirrespective files.Equal-keyed records from the lowest numbered SORTINnn file arewritten before those from the second input file, etc.NOEQUALS, the default, specifiesthat equal-keyed records from different files be written in random order.

order of equal-keyed records within each input file is always preserved during amerge, whether or not the EQUALS parameter is specified.

the EQUALS parameter is used with the SUM control statement, the first of theequal-keyed records is retained with the sum; all other records are deleted after thespecified field(s) have been summed.

/NOEQUALS can also be specified as a PARM option on the EXEC statement.If this option is specified both on the MERGE statement and as a PARM option, theMERGE specification takes precedence.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arFILES Parameter (Optional)

FILES=n parameter specifies the number of input files that an E32 exit will supplyto the merge.The n value can be any number up to 100.

the FILES parameter both on the MERGE statement and in the 24-bit pa-rameter list will cause SyncSort to terminate with a critical error.

FILES parameter cannot be specified as a PARM on the EXEC statement or in a$ORTPARM data set.

Parameter (Optional)

SKIPREC=n parameter instructs SyncSort to skip a decimal number of records beforethe input file is copied.The n records skipped are deleted from the input file beforeINCLUDE/OMIT processing, if specified, takes place.

SKIPREC parameter can only be specified for a MERGE FIELDS=COPY operation.SKIPREC cannot be specified for a merge of multiple SORTINnn data sets.

SKIPREC is specified as a PARM option as well as on the MERGE statement, thePhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aARM specification takes precedence.

2. SyncSort Control Statements2.41

MERGE

Parameter (Optional)

STOPAFT=n parameter specifies the number of records to be copied.These will bethe first n records after INCLUDE/OMIT and SKIPREC processing, if specified, havecompleted.

STOPAFT parameter can only be specified for a MERGE FIELDS=COPY operation.STOPAFT cannot be specified for a merge of multiple SORTINnn data sets.

STOPAFT is specified as a PARM option as well as on the MERGE statement, thePARM specification takes precedence.

MERGE Control Statements MERGEFIELDS=(1,5,CH,A,10,2,PD,D,30,4,BI,A)

.Sample MERGE Control Statement

sample MERGE statement specifies three merge control fields:

The first, or primary, control field begins in byte 1, is 5 bytes long, is in character

and is to be merged in ascending orhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ader.

second control field begins in byte 10, is 2 bytes long, is in packed decimal formatand is to be merged in descending order.

third control field begins in the third bit of byte 30, is 4 bytes long, is in binaryformat and is to be merged in ascending order.

=COPY,STOPAFT=200

.Sample MERGE Control Statement

MERGE statement specifies a copy operation.Only the first 200 records will becopied.

.42 Programmer'sGuide

MODS

Control Statement

MODS control statement specifies a user exit routine and is required with an exit.Refer to “Chapter 7.The Coding and Use of Exit Programs” for a detailed explanationof how to specify exit programs.

Control Statement Format

format of the MODS statement is illustrated below.MODS exit-name1=(parameters1),...,exit-name16=(parameters16)

parameters =

rhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,b  [,d]          ,N   ,S   ,C   ,E   ,X   ,T

a positional comma if the d value is omitted but the link-editing code is sup-plied.

.MODS Control Statement Format

an application has more than one exit, specify the exit-name parameter for each exit.Up to 16 exits can be http://www.wendangwang.come commas to separate multiple exit-name parameters.

-Name Parameter (Required)

exit-name parameter identifies the exit and provides additional information.Replace'exit-name' with an E followed by the appropriate exit number.The 16 valid exit-namesare listed below.

2. SyncSort Control Statements2.43

MODS

1

2Sort or MergePhase 3CopyE15E21

(merge only)

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarE39

.Phases and Permissible ExitsE31E35E37E38E39NameE61

exit-name parameter also provides the following information about the exit.

r value specifies the name of the user exit routine. Any valid name is ac-

. If the exit routine resides in a library, specify the member name or

name for the r value. For an exit coded in REXX, r represents the REXX

name.

b value specifies the exact or estimated decimal number of bytes the exit

requires in main storage.This number should include any additional

storage required by the exit (e.g., buffers, GETMAINs, etc.).Specify an

(without an E before the value) if the exact number is not known.

number should only include storage requirements below the 16-megabyte

.

exits have some additional storage requirements. REXX system http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amodules

control blocks need 26K, and each EXEC that is called will require 12K

storage. In addition to any variables that the EXEC uses, all special

variables will require storage (including space for a record).

d value identifies the DD statement name that specifies the library in

the exit routine resides.The JCL must include a DD statement speci-

each library in which an exit routine resides.If the exit routine is to be

in the input job stream, specify SYSIN for the d value.(If more than

exit routine is included in SYSIN, the exit routines must be specified in

numerical order by exit name.)b

.44 Programmer'sGuide

MODS

a Disk Sort, MAXSORT or PARASORT, an exit routine that is a load

residing in a library identified in a LINKLIB, STEPLIB or JOBLIB

statement does nothttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a require a d value specification or a DD statement de-

a module library in the JCL.If the d value is omitted, insert a positional

to indicate the missing value.For a Tape Sort, it is necessary to specify

LINKLIB, STEPLIB or JOBLIB DD statement and to include a DD state-

defining the library.

exit-name parameter also specifies link-editing codes: N, S, C, E, X, or T.If thelink-editing code is omitted, the installation setting determines whether or not the exitwill be link-edited.The delivered default is T; however, it may have been reset to N atinstallation.

, exit routines should be designed so that they do not require link-editing each timethey are used.Link-editing consumes system resources and increases sort/merge exe-cution time.

a link-editing code is specified, the name E10 is reserved and no Phase 1 exit orE61 exit can use this name as a Chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSECT or ENTRY name.Similarly, the names E20 andE30 are reserved and cannot be used by Phase 2 or Phase 3 exits.

N value specifies that link-editing is not required.Link-editing has al-

taken place and SyncSort can directly invoke the routine.

S value specifies that link-editing is required.This value can only be used

E11, E21 and E31 exits.The S value also indicates that the exit routine

be link-edited separately from other exit routines specified for the same

.

C value identifies a COBOL exit routine.COBOL exits must be link-

before execution time.Only COBOL E15 and E35 exits can be specified,

COBOL exits cannot be specified for a Tape Sort.

E value identifies a C exit routine.C exits must be link-edited before ex-

time.Only C E15 and/or E35 exits can be specified, and C exits cannot

specifihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed for a Tape Sort.

X value identifies a REXX exit routine.Only REXX E15 and E35 exits canbe specified, and REXX exits cannot be specified for a Tape Sort.

T value specifies that SyncSort will dynamically link-edit the exit routine

with other routines specified for the same sort/merge phase.SCEXT

2. SyncSort Control Statements2.45

MODS

MODS Control Statement

=(ADDREC1,600,MODLIB,N),E25=(ALTREC,500,SYSIN),E35=(ADDREC2,600,MODLIB,C)

.Sample MODS Control Statement

sample MODS statement specifies the following information:

An E15 exit is the first exit routine. ADDREC1 is the member name of the routine,

requires 600 bytes in main storage and resides in a library referenced by theDD statement named MODLIB.The routine does not require link-editing.

E25 exit is the second exit routine.ALTREC is thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe member name of the routinewhich requires 500 bytes in main storage.The exit is included in the SYSIN inputstream.Because N is not specified, this routine will be link-edited.

E35 exit is the third exit routine.ADDREC2 is the member name of the routine,which requires 600 bytes in main storage and resides in a library referenced by theDD statement named MODLIB.This routine is a COBOL exit which has been link-edited before execution time.

of JCL-initiated applications with exit routines are illustrated in “Chapter 4.JCL and Sample JCL/Control Statement Streams”.

.46 Programmer'sGuide

OMIT

Control Statement

to “INCLUDE/OMIT Control Statement” on page 2.16 for an explanation of the

2. SyncSort Control Statements2.47OMIT control statement.

OUTFIL

Control Statement

OUTFIL control statement describes the output file or http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afiles.It is required to ac-complish these three tasks:

Create multiple output http://www.wendangwang.come the SortWriter facility.Reformat records after E35 processing.

OUTFIL control statement cannot be used with MAXSORT.

OUTFIL parameters associated with each of these tasks are listed below:

Creating multiple output files: FILES, FNAMES, INCLUDE/OMIT, STARTREC,

, SAVE, OUTREC, CONVERT, SPLIT

the SortWriter facility: HEADER1, HEADER2, LINES, NODETAIL,SECTIONS, TRAILER1, TRAILER2

records: OUTREC

Control Statement Format

format for the OUTFIL statement is illustrated below.

.48 Programmer'sGuide

OUTFIL OUTFIL

fileid   FILES=        (fileid1 [,fileid2]...)

ddname   ,FNAMES=       (ddname1 [,ddname2] ...)

ALL  NONE     ,INCLUDE        ,AND,        = (c1    http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,&amp;,  c2...  )    ,OMIT      ,OR,        , ,

[,STARTREC=n]

[,ENDREC=n]

[,SAVE]

[,SPLIT]

[,OUTREC=(field1 [,field2]...)]

[,CONVERT]

[,HEADER1=(field1 [,field2]...)]

[,HEADER2=(field1 [,field2]...)]

[,TRAILER1=(field1 [,field2]...)]

[,TRAILER2=(field1 [,field2]...)]

[,SECTIONS=(field1 [,field2]...)]

n   ,LINES=   ANSI     (ANSI,n)

[,NODETAIL]

.OUTFIL Control Statement Format

Multiple Output Capability

the OUTFIL control statement to create multiple files without making multiplepasses through the input data.The output files can be treated the same or differently: The output files can contain the same or different records.

2. SyncSort Control Statements2.49

OUTFIL

The records in the output files can be identically or differently formatted.If the inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aput file(s) are variable length, the output files may be either variable length

fixed length.

that all the output files will be sequenced in the same way, as specified on the SORTor MERGE statement.If you need to sort the output files differently, you should usePipeSort, a Syncsort product that works with SyncSort MVS to reduce total elapsed timeby generating multiple, differently sequenced output files from a single read of the inputdata.

SortWriter Capability

SortWriter capability of OUTFIL can produce completely formatted reports.The re-port writing features, which can be specified differently for each output file, can accom-plish these tasks:

Arrange the report into pages.Divide the report into sections.Format headers and trailers for sections, pages, and the complete report.Create multiple lines of output from each input record.Conhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1avert and edit numeric data.Provide TOTAL and SUBTOTAL capabilities for data fields in a specific part of a

.

MIN, MAX, AVERAGE, SUBMIN, SUBMAX and SUBAVG capabilities fordata fields in a specific part of a report.

COUNT and SUBCOUNT capabilities for records in a specific part of a re-port.

formatted, output files can be assigned to any tape, disk, or unit record device forsubsequent printing.

Parameter (Optional)

FILES parameter connects the OUTFIL statement with one or more output files.The files specified on this parameter, along with any specified on the FNAMES parame-ter, will constitute the ddnames to receive output for this OUTFIL specification.The format of the FILES parameter is illustrated in the following figure.

.50 Programmer'sGuide

OUTFIL   fileid   FILES=    (fileid1[,fileid2] ...)

:

=  xx

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparFigure25.FILES Parameter Format Chart

fileid identifies the output file and connects the OUTFIL statement with the corre-sponding SORTOUT, SORTOFx or SORTOFxx DD statement.For example, FILES=OUTconnects the OUTFIL statement with the SORTOUT DD statement.Similarly, FILES=1connects the OUTFIL statement with the SORTOF1 DD statement, and FILES=01 con-nects the OUTFIL statement with the SORTOF01 DD statement.The x can be any al-phanumeric character or special character allowed by JCL DD statements.

multiple output files have identical specifications (that is, identical record selection,record reformatting and report writing specifications), the FILES and/or FNAMES pa-rameter can connect the OUTFIL statement with more than one DD statement.For ex-ample, FILES=(OUT,02,03) connects the OUTFIL statement with the SORTOUT,SORTOF02 and SORTOF03 DD statements.Such a set of output files is termed anOUTFIL group.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1af multiple output files have different specifications, then each file is specified on a sepa-rate OUTFIL statement with one FILES and/or FNAMES parameter on each statement.If a SORTOUT ddname is defined in the JCL and does not appear in any FILES orFNAMES specification, it will be written to without any OUTFIL processing.If an inlineE35 exit has been specified, OUTFIL is ignored.

neither a FILES nor FNAMES parameter is specified on an OUTFIL statement, thedefault ddname of SORTOUT will be used.If a 4-byte ddname prefix is in effect, thedefault SORTOUT ddname will be ppppOUT, where pppp is the prefix; adding FILES=xxwould connect to the ppppOFxx DD statement.

Parameter (Optional)

FNAMES parameter connects the OUTFIL statement with one or more output files.The files specified on this parameter, along with any specified on the FILES parameter,will constitute the ddnames to receive output for this OUThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aFIL specification.

format of the FNAMES parameter is illustrated in the following figure.

2. SyncSort Control Statements2.51

OUTFIL   ddname  FNAMES=    (ddname1 [,ddname2] ...)

.FNAMES Parameter Format Chart

is a 1- to 8-character ddname that corresponds to a DD statement provided in theJCL.

multiple output files have identical specifications (that is, identical record selection,record reformatting and report writing specifications), the FNAMES and/or FILES pa-rameter can connect the OUTFIL statement with more than one DD statement.For ex-ample, FNAMES=(FILE1OUT,FILE2OUT,FILE3OUT) connects the OUTFIL statementwith the three listed DD statements.Such a set of output files is termed an OUTFILgroup.

multiple output files have different specifications, then each file is specified on a sepa-rate OUTFIL statement with one FNAMES and/or FILES parameter http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aon each statement.If a SORTOUT ddname is defined in the JCL and does not appear in any FILES orFNAMES specification, it will be written to without any OUTFIL processing.If an inlineE35 exit has been specified, OUTFIL is ignored.

neither a FILES nor FNAMES parameter is specified on an OUTFIL statement, thedefault ddname of SORTOUT will be used.If a 4-byte ddname prefix is in effect, thedefault SORTOUT ddname will be ppppOUT, where pppp is the prefix.

/OMIT Parameter (Optional)

the INCLUDE or OMIT parameter to indicate which records are to be includedin or omitted from each output file.These parameters let you create multiple output fileswhich contain different records.The default is to include all sorted or merged records inthe output file.

format for the INCLUDE/OMIT parameter is illustrated below:

.52 Programmer'sGuide

OUTFIL   ALL  NONE     INCLUDE       = (c1  OMhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aIT       c represents a comparison.       ,AND,        ,&amp;,  c2...  )      ,OR,        , ,      Each comparison has this format:

.INCLUDE/OMIT Parameter Format

“INCLUDE/OMIT Control Statement” on page 2.16 for the detailed format of a com-parison.The FORMAT=f parameter, which is permitted for the INCLUDE/OMIT controlstatement, is not permitted for the INCLUDE/OMIT parameter.Field formats must bespecified on a field-by-field basis.

comparison determines which records are included or omitted.When no data recordsare to be included in the output file(s), for example, when running a test, specify eitherINCLUDE=NONE or OMIT=ALL.

:The location within the data records of the fields specified in the INCLUDE/OMITparameter will be based on the formatting of the record after processing by an E15/E32exit, the INREC control statement, the OUTREC control statement, and an E35 exit, butbefore prochttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aessing due to the OUTREC and/or report writing parameters of the OUTFILcontrol statement.

following four parameters (STARTREC, ENDREC, SAVE and SPLIT) are related tothe previous parameter (INCLUDE/OMIT) in that they specify records to be included forOUTFIL processing.However, these four options specify records in bulk rather thanthrough a comparison condition.

Parameter (Optional)

the STARTREC=n parameter to specify the record number n of the first record to beprocessed by the OUTFIL specification in effect.All records prior to the specified recordwill be ignored for the OUTFIL group.The record number is determined by the sequenceof records presented for OUTFIL processing.

Parameter (Optional)

the ENDREC=n parameter to specify the record number n of the last record to beprocessed by the OUTFIL specification in effect.All records after the specified recordwill be ignoredhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a for the OUTFIL group.The record number is determined by the sequenceof records presented for OUTFIL processing.

2. SyncSort Control Statements2.53

OUTFIL

Parameter (Optional)

SAVE to include records for OUTFIL processing that have not been included in anyother OUTFIL group.

SAVE is specified on more than one OUTFIL group, then each of these OUTFIL groupsget the records that were discarded from all other OUTFIL groups that do not have SAVE.The OUTFIL INCLUDE/OMIT parameter is mutually exclusive with the SAVE parame-ter.Only one of these parameters can be specified for an OUTFIL group.

that if the SORTOUT data set has not been associated with any OUTFIL statementbut is present in the JCL, the SORTOUT data set will receive a copy of all records priorto OUTFIL processing.This does not affect the SAVE operation, since SAVE is onlypertinent to other OUTFIL group specifhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aications.

Parameter (Optional)

OUTREC parameter indicates how the records are to be formatted in each output file.This parameter lets you create multiple output files which contain differently formattedrecords.

the records in all multiple output files are formatted and edited identically, it ismore efficient to specify a single OUTREC control statement rather than severalOUTREC parameters.

OUTREC parameter reformats the records that are to be included in the output file(s)after E35 processing, if specified.If no additional reformatting is required, omit this pa-rameter.

references to field positions specified in the OUTREC parameter refer to the recordafter processing by an E15 exit, the INREC control statement, the OUTREC controlstatement and an E35 exit but before insertion of ANSI control characters.

format of the OUTREC parameter is illustrated below.OUTREC=(http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afield1[,field2]...)

.OUTREC Parameter Format

format of the OUTFIL OUTREC parameter is generally identical to the format ofFIELDS parameter of the OUTREC control statement.(See the subsections dealing withthe FIELDS parameter in “OUTREC Control Statement” on page 2.74.)Note, however,that FIELDS= is not used with OUTFIL OUTREC.In addition, OUTFIL OUTREC ac-cepts a subparameter that cannot be specified on the OUTREC control statement:

.54 Programmer'sGuide

OUTFIL

[n]/The / subparameter indicates the end of a line and can be used to create

output lines from a single input record.Multiple slashes (coded

//.../ or n/) can be used to specify leading, trailing or embedded blank lines.

the beginning or end of the OUTREC parameter, n/ produces n blank

. Embedded within the OUTREC parameter, n/ produces n-1 blank

.

/ subparamehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ater is most useful for its ability to accommodate records

lengths exceed the width of the physical page.For an example use

the / subparameter, see “Printing Input Records on Multiple Output

” on page 3.27.

/ subparameter may not be used when LINES=ANSI or

=(ANSI,n) has also been specified on the OUTFIL statement.

Parameter (Optional)

CONVERT parameter is used in conjunction with the OUTREC parameter to convertvariable length records to fixed length records.Refer to the OUTREC control statementfor a detailed explanation on the use of this parameter.

:If CONVERT is specified, the OUTREC parameter must also be specified.

Parameter (Optional)

SPLIT parameter of the OUTFIL control statement causes output records to be dis-tributed in rotation among files in an OUTFIL group.

OUTFIL group is a set of output filehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as specified by the FILES parameter on theOUTFIL control statement.The FILES parameter associates output files with corre-sponding SORTOFx or SORTOFxx DD statements (for example, SORTOF01, SORTOF02,SORTOF03.)For a description of the FILES parameter, see “FILES Parameter(Optional)” on page 2.50.

the normal case, when the SPLIT parameter is not used, the output files in the groupwill contain the same records.SPLIT distributes the output records.The followingOUTFIL control statement will distribute records among three output files:OUTFIL FILES=(01,02,03),SPLIT

.Sample OUTFIL Control Statement with SPLIT

2. SyncSort Control Statements2.55

OUTFIL

the above example, the first record will be written to the SORTOF01 data set; thesecond, to SORTOF02; the third, to SORTOF03.The fourth record will be written toSORTOF01 again, and so on in round-robin fashion.

OUTFIL controlhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a statement can contain an INCLUDE/OMIT and an OUTREC pa-rameter, in which case the selected and reformatted subset of records will be distributedamong the output files.

that the SPLIT parameter cannot be used with any report writing (SortWriter)functions.Specifically, report writing parameters (HEADERn, TRAILERn, SECTIONS,LINES, NODETAIL) cannot be specified on the OUTFIL control statement that definesthe output group.

can be used with BatchPipes/MVS; that is, the output records can be distributedamong BatchPipes/MVS data sets.

/HEADER2 Parameters (Optional)

SortWriter facility provides three types of headers:

HEADER1, the report headerHEADER2, the page headerHEADER3, the section header.

and HEADER2 are parameters of the OUTFIL control statement.HEADER3is a subparameter of OUTFIL's SECTIONS parameter.Refer to “SECTIONS Parameter(Optional)” onhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a page 2.67 for an explanation of how to specify HEADER3.

three types of headers function independently of each other.Each serves a differentpurpose.

HEADER1 provides a header or a possible title page for the entire report.It appears

once at the beginning of the report on its own page.

provides a page header or a running head for each page defined by theLINES parameter. It appears at the beginning or top of each page.

provides a section header that appears at the beginning of each specifiedsection and, optionally, at the top of each page (or directly below any HEADER2).  The chart below illustrates the format for HEADERs.The field entries represent thesubparameters that can be specified for each HEADER entry.

.56 Programmer'sGuide

OUTFIL HEADER1=(field1[,field2]...)

=(field1[,field2]...)

=(field1[,field2]...)

.HEAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aDER Parameter Format Chart

following HEADER Subparameters Format Chart illustrates and defines the avail-able subparameters.Each subparameter constitutes a separate field of the HEADER. [ c: ]             [ n ]X[ n ]'literal string' [ n ] /p,l&amp;DATE&amp;DATE=(m1m2m3m4)&amp;TIME&amp;TIME=(hp)&amp;PAGE

.

:HEADER Subparameter Format ChartUse the c: subparameter to define the column in which the

field should begin.

in conjunction with the X, 'literal string', and / subpa-

, the n value defines the number (1-4095) of repe-

for each entry.

the X subparameter to define the number of spaces.It

be coded to the immediate right of the n value, if speci-

.For more than 4095 spaces, two or more nX values

be specified.

the 'literal string' subparameter to define a literal string.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparSpecify the number of repetitions by coding n immediately

it.An apostrophe within a literal string must be spec-

as a double apostrophe; for example, C 'O&quot;Leary'.

the / subparameter to indicate the end of a line, force a

return and separate text lines of a header.Multiple

(//.../ or n/) can be used to specify leading, trailing or

blank lines. At the beginning or end of a header,nX'literalstring'/

2. SyncSort Control Statements2.57

OUTFIL

,l

&amp;DATE&amp;DATE=(m1m2m3m4)

.58 Programmer'sGuiden/ produces n blank lines.Within a header, n/ produces n-1blank http://www.wendangwang.come the p and l subparameters to include a field (or fields)within a record in the header.For a HEADER1, the field(s)will be extracted from the first record in a file; for aHEADER2, the field(s) will be extracted from thehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a first recordon a page; for a HEADER3, the field(s) will be extracted fromthe first record in a section.p is the starting position of thefield in the record; l is the length in bytes (1-255) of the field.Any number of fields can be specified.(Contiguous fieldswithin a record can be specified with a single p,l entry, buttheir combined length cannot exceed 255 bytes.)The specifiedfield(s) should be a character or alphanumeric string or anumber in printable format, and the field(s) cannot be con-verted or edited.The &amp;DATE subparameter specifies the current system dateand requires 8 bytes to display mm/dd/yy.This form of the &amp;DATE subparameter generates the currentsystem date and controls the formatting of the date.You canspecify the position of the year, month, and date; specify aseparator character; and choose between 2-digit and 4-digityear representation.The positions m1 through m4 represent masks used to formatthe date.To http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aspecify the position of the month, day and year,replace the m1, m2 and m3 positions, in any order, with M forthe month (01-12), D for the day (01-31), and either Y or 4 forthe year (where Y is a 2-digit year and 4 is a 4-digit year).Replace the m4 position with a separator character.For example, to print the date with the form yy-mm-dd, spec-ify &amp;DATE=(YMD-).For December 31, 1997, the date wouldappear as &quot;97-12-31&quot;.A blank used as the separator character must be enclosed inapostrophes.An apostrophe used as the separator charactermust be specified as two apostrophes enclosed within apos-trophes ('''').The field for this form of&amp;DATE requires 8 bytes for a 2-digityear representation and 10 bytes for a 4-digit year. The M,D, and Y or 4 may only appear once in the mask.All fourpositions must be specified.

&amp;TIME

&amp;TIME=hp

&amp;PAGE OUTFIL The &amp;TIME subparameter specifies the current tihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ame of dayand requires 8 bytes to display hh:mm:ss, where hh is in24-hour format.This form of the &amp;TIME subparameter generates the currentsystem time of day and controls the formatting of the time.You can print the time in 24-hour or 12-hour formats andspecify the separator character between the hours, minutesand seconds.The format for 24-hour time is hhpmmpss, where hh repres-ents the hour (00-23), mm represents minutes (00-59), ss re-presents seconds (00-59), and p represents the separatorcharacter as specified by p in the &amp;TIME=hp subparameter.The format for 12-hour time is hhpmmpss nn, where hh re-presents the hour (01-12), mm represents minutes (00-59), ssrepresents seconds (00-59), and p represents the separatorcharacter as specified by p in the &amp;TIME=hp subparameter.The nn is &quot;am&quot; or &quot;pm&quot; as appropriate.To select 12-hour mode specify h as '12'; to select 24-hourmode specify h as '24'.The p spechttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aification represents thecharacter to use as a separator.For example, to display the time in a 12-hour format with aperiod as a separator, specify &amp;TIME=(12.).At 22:43:23hours, the time would appear as &quot;10.43.23 pm&quot;.A blank used as the separator character must be enclosed inapostrophes.An apostrophe used as the separator charactermust be specified as two apostrophes enclosed within apos-trophes ('''').The field for this form of the &amp;TIME subparameter requires8 bytes for the 24-hour format and 11 bytes for the 12-hourformat.The &amp;PAGE subparameter sequentially numbers logical

of the output report and requires 6 bytes.It produces

6-digit sequential page number, right justified with leading

suppressed.&amp;PAGE is ignored for HEADER1.

2. SyncSort Control Statements2.59

OUTFIL

for Specifying HEADER Subparameters

the following guidhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aelines when you specify HEADER subparameters:

Separate subparameters with commas, except between c:and another subparameter.

are optional for the / subparameter.

literals in single quotes.

blank fields of n bytes as nX.

headings (i.e., headings specified with fewer blanks than the logical record

(LRECL) of the output record) are automatically padded on the right with

.

a heading exceeds the logical record length (LRECL) of the output record, use the

statement or the OUTREC parameter to expand the output record length

that it is at least as long as the longest header.For example, if the longest header

115 characters and the output record length is 80 bytes, use the OUTREC state-

or the OUTREC parameter to insert a blank in position 115 of the output re-

.This will cause bytes http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a81 through 115 to be padded with blanks.

Parameters (Optional)

SortWriter facility provides three types of trailers:

TRAILER1, the report trailerTRAILER2, the page trailerTRAILER3, the section trailer.

and TRAILER2 are parameters of the OUTFIL control statement; TRAILER3is a subparameter of OUTFIL's SECTIONS parameter.Refer to “SECTIONS Parameter(Optional)” on page 2.67 for an explanation of how to specify TRAILER3.

three types of trailers function independently of each other.Each serves a differentpurpose:

TRAILER1 provides a trailer or a possible summary for the entire report.It appears

once at the end of the report on its own page.

provides a page trailer for each page defined by the LINES parameter.

appears at the end of each page.

provides a section trailer that appears at the end of http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeach specified section

serves as a conclusion or summary for that section.

, TRAILER2 and TRAILER3 also provide TOTAL, SUBTOTAL, MIN,SUBMIN, MAX, SUBMAX, AVG, SUBAVG, COUNT, SUBCOUNT, COUNT15 andSUBCOUNT15 capabilities at report, page and section levels.

.60 Programmer'sGuide

OUTFIL

chart below illustrates the format for TRAILERs.Its field entries represent the

that can be specified for each TRAILER entry.

=(field1[,field2]...)TRAILER2=(field1[,field2]...)TRAILER3=(field1[,field2]...)

.TRAILER Parameter Format Chart

following TRAILER Subparameters Format Chart illustrates and defines the avail-

subparameters.Each subparameter constitutes a separate field of the TRAILER.  [n ] X  [n ] 'literal string'   [n ] /  p,l  &amp;DATE  &amp;DATE=(m1m2m3m4)  &amp;TIME  &amp;TIME=(hp)  &amp;PAGE     TOTAL/Thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOT [c:]     SUBTOTAL/SUB        MIN   ,Mm      SUBMIN  = (p,l,f     ,EDIT=(...)   [,SIGNS=(...)] [,LENGTH=(n)])     MAX          SUBMAX    AVG    SUBAVG     COUNT  SUBCOUNT  COUNT15  SUBCOUNT15

.

:TRAILER Subparameters Format ChartUse the c: subparameter to define the column in which the spec-

field should begin.

in conjunction with the X, 'literal string', and / subparame-

, the n value defines the number (1-4095) of repetitions for

entry.

the X subparameter to define the number of spaces. It must

coded to the immediate right of the n value, if specified. For

2. SyncSort Control Statements2.61nX

OUTFIL

than 4095 spaces, two or more nX values should be speci-

.

'literalstring'Use the 'literal string' subparameter to define a literal string.

the numberhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a of repetitions by specifying n immediately

it.An apostrophe within a literal string must be specified

a double apostrophe; for example, C 'O&quot;Leary'.

the / subparameter to indicate the end of a line, force a car-

return and separate text lines of a trailer. Multiple slashes

(coded //.../ or n/) can be used to specify leading, trailing or em-

blank lines. At the beginning or ending of a trailer, n/

n blank lines. Within a trailer, n/ produces n-1 blank

.

the p and l subparameters to include a field (or fields) within

record in the trailer. For a TRAILER1, the field(s) will be ex-

from the last record in a file; for a TRAILER2, the field(s)

be extracted from the last record on a page; for a TRAILER3,

field(s) will be extracted from the last record in a section. p

thehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a starting position of the field in the record; l is the length

bytes (1-255) of the field. Any number of fields can be specified.

(Contiguous fields within a record may be specified with a single

,l entry, but their combined length may not exceed 255 bytes.)

specified field(s) should be a character or alphanumeric

, or a number in printable format, and the field cannot be

or edited.

any variable length record contains only a portion of the bytes

a specified field, those bytes will be included in the trailer and

will be substituted for the missing bytes.

&amp;DATEThe &amp;DATE subparameter specifies the current system date and

8 bytes to display mm/dd/yy./p,l

&amp;DATE=(m1m2m3m4)This form of the &amp;DATE subparameter generates the current

date and controls the formatting of the date.You canhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

the position of the year, month, and date; specify a sepa-

character; and choose between 2-digit and 4-digit year rep-

.

positions m1 through m4 represent masks used to format the

.To specify the position of the month, day and year, replace

m1, m2 and m3 positions, in any order, with M for the month

(01-12), D for the day (01-31), and either Y or 4 for the year

(where Y is a 2-digit year and 4 is a 4-digit year).Replace the

position with a separator character.

.62 Programmer'sGuide

&amp;TIME

&amp;TIME=hp

&amp;PAGE

/TOT OUTFIL For example, to print the date with the form yy-mm-dd, specify&amp;DATE=(YMD-).For December 31, 1997, the date would appearas &quot;97-12-31&quot;.The field for this form of&amp;DATE requires 8 bytes for a 2-digityear representation and 10 bytes for a 4-digit year. http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aThe M, D, andY or 4 may only appear once in the mask.All four positions mustbe specified.The &amp;TIME subparameter specifies the current time of day andrequires 8 bytes to display hh:mm:ss, where hh is in 24-hourformat.This form of the &amp;TIME subparameter generates the currenttime of day and controls the formatting of the time.You canprint the time in 24-hour or 12-hour formats and specify theseparator character between the hours, minutes and seconds.The format for 24-hour time is hhpmmpss, where hh representsthe hour (00-23), mm represents minutes (00-59), ss representsseconds (00-59), and p represents the separator character asspecified by p in the &amp;TIME=hp subparameter.The format for 12-hour time is hhpmmpss nn, where hh repres-ents the hour (01-12), mm represents minutes (00-59), ss repres-ents seconds (00-59), and p represents the separator characteras specified by p in the &amp;TIME=hp subparameter.The nn is&quot;am&qhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1auot; or &quot;pm&quot; as appropriate.To select 12-hour mode specify h as '12'; to select 24-hour modespecify h as '24'.The p specification represents the character touse as a separator.For example, to display the time in a 12-hour format with a pe-riod as a separator, specify &amp;TIME=(12.).At 22:43:23 hours, thetime would appear as &quot;10.43.23 pm&quot;.The field for this form of the &amp;TIME subparameter requires 8bytes for the 24-hour format and 11 bytes for the 12-hour format.The &amp;PAGE subparameter sequentially numbers logical pagesof the output report and requires 6 bytes. It produces a 6-digitsequential page number, right justified with leading zeros http://www.wendangwang.come the TOTAL subparameter to specify that numeric data is to

accumulated and totaled at the end of a report, logical page

section.

2. SyncSort Control Statements2.63

OUTFIL

/SUB

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aN

.64 Programmer'sGuideAfter including the results in the appropriate trailer, the accu-mulator resets to zero. TOTALs appear in printable format.If aSyncSort editing mask is used for totaled data, the length of theoutput field is determined by the maximum permissible lengthof the data format, not by the specified length of the input field.This means that the default is to display 10 digits for BI and FIfields, and 15digits for PD, ZD, and CSF or FS fields.Inter-nally, SyncSort maintains up to 15 digits for all data formats.Thus, if a BI or FI field total could exceed 10 digits, you shouldspecify the LENGTH and/or EDIT subparameters to override thelength of the output http://www.wendangwang.come the SUBTOTAL subparameter to generate a running totalof a field at the end of a report, logical page or section. Thissubparameter functions like the TOTAL subparameter except theaccuhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amulator does not reset to zero. SUBTOTALs appear inprintable format.If a SyncSort editing mask is used for subto-taled data, the length of the output field is determined by themaximum permissible length of the data format, not by thespecified length of the input field.This means that the defaultis to display 10 digits for BI and FI fields, and 15digits for PD,ZD, and CSF or FS fields.Internally, SyncSort maintains up to15 digits for all data formats.Thus, if a BI or FI field total couldexceed 10 digits, you should specify the LENGTH and/or EDITsubparameters to override the length of the output http://www.wendangwang.come the MIN subparameter to obtain the minimum numericvalue of an input field for all records within the report, logicalpage or section.This value will be displayed in printable http://www.wendangwang.come the SUBMIN subparameter to obtain the running minimumnumeric value of an input field for all records within the rehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aportup to the point of the TRAILER.This value will be displayed inprintable http://www.wendangwang.come the MAX subparameter to obtain the maximum numericvalue of an input field for all records within the report, logicalpage or section.This value will be displayed in printable http://www.wendangwang.come the SUBMAX subparameter to obtain the running maximumnumeric value of an input field for all records within the reportup to the point of the TRAILER.This value will be displayed inprintable http://www.wendangwang.come the AVG subparameter to obtain the average numeric valueof an input field for all records within the report, logical page orsection.This value will be displayed in printable format.

SUBAVG

=(pattern)

=(...)

=(n)

OUTFIL Use the SUBAVG subparameter to obtain the running averagenumeric value of an input field for all records wihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athin the reportup to the point of the TRAILER.This value will be displayed inprintable http://www.wendangwang.come the p subparameter to indicate the position of the first byteof the numeric http://www.wendangwang.come the l subparameter to indicate the length of the numericfield.Permissible lengths are 1-4 bytes for BI or FI, 1-8 bytes forPD, 1-15 bytes for ZD, and 1-16 for CSF or FS with a 15-digitlimit.To determine the length of the output field, refer to “Howto Convert Numeric Data” on page 2.82.For the (SUB)TOTAL and (SUB)AVG functions, fields are totaledinternally as 8-byte PD fields.An overflow condition will occurif the positive or negative value of a totaled or subtotaled fieldexceeds the value that can be represented by such fields, and theexecution will terminate with an error http://www.wendangwang.come the f subparameter to indicate the format of the numericfield.Replace f with BI, FI, PD, ZD, CSF or http://www.wendanghttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1awang.come the Mm subparameter to indicate that one of the 26SyncSort-supplied masks (M0 - M25) be used to format a field.Replace m with the mask number.The default is M0.For de-tails, refer to “The Mm Subparameter (Editing Masks)” on http://www.wendangwang.come the EDIT=(pattern) subparameter to indicate that a user-provided editing mask be used to format a field.For details, referto “The EDIT Subparameter” on page http://www.wendangwang.come the SIGNS subparameter to specify leading and/or trailingsigns that will appear before or after the edited number.Fordetails, refer to “The SIGNS Subparameter” on page http://www.wendangwang.come the LENGTH subparameter to alter the length of a field de-termined by the edit pattern and the internal field format.Fordetails, refer to “The LENGTH=n Subparameter” on page http://www.wendangwang.come the COUNT subparameter to obtain a count of the number

records in either the entire reporthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a or a specific part of the re-

.In a TRAILER1, this field will contain a count of the total

of data records in the report.In a TRAILER2, it will

a count of the number of data records on each page.In

TRAILER3, it will contain a count of the number of data re-

in each section.The count will be the number of data re-

before any multi-line OUTREC processing has been done.

2. SyncSort Control Statements2.65

OUTFIL

number will be a right-justified 8-digit field with leading

suppressed.The maximum value is 99999999.

This subparameter is identical to the COUNT subparameter ex-

for the allowable size of the count number.For COUNT15

number will be a right-justified 15-digit field with leading

suppressed.The maximum value is 999999999999999.

the SUBCOUNT subparhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aameter to obtain a running, or cu-

, count of the number of records throughout a report. In

TRAILER1, this field will contain a count of the total number

data records in the report. In a TRAILER2, it will contain a

count of the number of data records on a page-by-

basis. In a TRAILER3, it will contain a cumulative count

the number of data records on a section-by-section basis.The

will be the number of data records before any multi-line

processing has been done.This number will be a

-justified, 8-digit field with leading zeros suppressed. The

value is 99999999.

subparameter is identical to the SUBCOUNT subparameter

for the allowable size of the count number.For

the number will be a right-justified 15-digit field

leading zeros suppressed.The maximum valhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aue is

.SUBCOUNTSUBCOUNT15

for Specifying TRAILER Subparameters

the following guidelines when you specify TRAILER subparameters:

Separate fields with commas, except for /, where commas are optional.Enclose literals in single quotes.Specify blank fields of n bytes as nX.If a SyncSort editing mask is used for totaled or subtotaled data, either by specifica-

or by default, the length of the generated pattern will be determined by the

permissible length supported for that data format, regardless of the actual

of the field being totaled or http://www.wendangwang.come the LENGTH subparameter to

the length of the pattern.

trailers (i.e., trailers specified with fewer blanks than the logical record length

(LRECL) of the output record) are automatically padded on the right with blanhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aks.

a trailer exceeds the logical record length (LRECL) of the output record, use the

statement or the OUTREC parameter to expand the output record length

that it is at least as long as the longest header.For example, if the longest trailer

115 characters and the output record length is 80 bytes, use the OUTREC state-

.66 Programmer'sGuide

OUTFIL

or the OUTREC parameter to insert a blank in position 115 of the output re-

.This will cause bytes 81 through 115 to be padded with blanks.

Parameter (Optional)

SECTIONS parameter allows the output report to be divided into sections.

format of the SECTIONS parameter is illustrated below.SECTIONS=(field1[,field2]...)

field is specified as follows:

,l[,subparameter1] [,subparameter2]...

.SECTIONS Parameter Format Chart

SECTIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aONS parameter identifies the control field(s) that determine, or control, sec-tion breaks.More than one control field can be specified to subdivide a report withinsections.However, if more than one control field is specified, the specifications must bemade in major to minor order.A major control field break causes all minor control fieldsto break at the same time.

control field is identified by its position p and length l.

position value indicates the first byte of the field relative to the beginning

the record after processing by an E15/E32 exit, the INREC statement, the

statement and an E35 exit, if specified, but before processing by the

parameter and other report writing parameters of the OUTFIL

, if specified.

length value indicates the length of the field.The length must be an in-

number of bytes and cannot exceed 256 bytes.lhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

each control field, one or more of the following subparameters may be specified: SKIP,HEADER3 or TRAILER3.The SECTIONS subparameters are described below.   P  ,SKIP=   nL          [ ,TRAILER3=(...) ] [ ,HEADER3=(...) ] [ ,PAGEHEAD]

35.SectionsSubparameter

2. SyncSort Control Statements2.67

OUTFIL

SKIP subparameter specifies the amount of spacing that should

after a section is completed. This spacing will follow imme-

after the last TRAILER3 for that section, if specified.

=nL specifies that the next line of the report will appear after

number of blank lines. SKIP=P specifies a page break following

completion of a section.

HEADER3 subparameter specifies a section header or title that

appear at the start of each new section. The HEADER3 format

identical to the format of the HEAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aDER1/HEADER2 parameters.

(See HEADER1/ HEADER2 Parameters for details.)

TRAILER3 subparameter specifies a section trailer that will

at the end of each section. The TRAILER3 format is identical

the format of the TRAILER1/TRAILER2 parameters. (See

/ TRAILER2 Parameters  for details.)

PAGEHEAD subparameter may be specified in conjunction

the HEADER3 subparameter.The PAGEHEAD subparameter

that the HEADER3 appear at the top of each page follow-

any HEADER2, as well as at the start of each new section.

is ignored if no HEADER3 is specified.HEADER3TRAILER3PAGEHEAD

control field may be specified without any subparameters.This allows multiple non-contiguous control fields to be specified for each SECTIONS break field.

Parameter (Optional)

the LINES parameter to define the logical pages http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aconstituting a report.The pages canbe defined in three ways:

Using the carriage control characters automatically supplied by SyncSort http://www.wendangwang.coming ANSI control characters supplied by the http://www.wendangwang.coming a combination of the above two methods.

of which method is selected, the number of lines defining a logical page mustbe equal to or greater than the total number of lines, including blank lines, required forall HEADER2, HEADER3, TRAILER2 and TRAILER3 entries plus at least one record.If multi-line OUTREC is used, all lines produced from each input record will be writtento the same logical page.

format of the LINES parameter is illustrated below:

.68 Programmer'sGuide

OUTFIL   n  LINES =   ANSI   (ANSI,n)

.

=nLINES Parameter Format Chart

LINES=n is specified, paging is automatic and carriage conhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atrol characters are added

the beginning of each record by SyncSort.Because SyncSort requires one byte for a

character, the LRECL specified in the SORTOUT, SORTOFx or SORTOFxx DD

must be one byte longer than the number of bytes specified for the output re-

length.

n as a value from 1 to 255.If report-writing parameters are specified for the file(s)

(e.g., HEADERs, TRAILERs, SECTIONS), the default is LINES=60.

LINES=n specification works in conjunction with any HEADERs and TRAILERs you

specified as follows:

HEADER1, if specified, prints as a preface to the report.Its page is not numbered.An automatic page break occurs after HEADER1.Every nth line after the completion

HEADER1 will signal the start of a new page.

HEADER2 entry, if present, is the first line(s) on each page, followed by any

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a3 entries that might be triggered either by control breaks or by PAGEHEAD

in the SECTIONS parameter. HEADER2 is part of the logical page.

HEADER3 entry, if present, is part of a section of the report.It prints as a header

the separate report sections.HEADER3s appear in major to minor order accord-

to the order of their associated sections.

PAGEHEAD is specified, HEADER3 prints immediately below HEADER2, if

, or at the top of the page if a HEADER2 is not specified.A HEADER3 will

print near the end of a page if there is not sufficient room on that page for at least

data record and a TRAILER2, if specified.

TRAILER3 entry, if present, is part of a section of the report.It prints as a con-

or summary for the separate report sections.TRAILER3s will appear in

to minor order according to the order of thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeir associated sections.

TRAILER2 entry, if present, will be the last line(s) on the logical page, preceded

any TRAILER3s triggered by coincidentally occurring control breaks.TRAILER2

part of the logical page.

will be the last page of the entire report.Its page is not numbered.

2. SyncSort Control Statements2.69

OUTFIL

, when LINES=n is specified, all HEADER2, HEADER3, TRAILER2 and

entries will be included as part of n (the total number of lines in a logical

) and will print as described above.

=ANSI

LINES=ANSI is specified, user-provided ANSI control characters define the logical

.The first byte of each output record must contain an ANSI control character (in-

, for example, by an E35 program) which is valid for the specified output device

.For example, insehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arting a '0' in byte 1 of the output records produces double-spaced

.

ANSI control characters which can be used with the LINES=ANSI specification are

in the ANSI Control Character Chart below.

printed output is requested, the ANSI control characters do not print as part of the

record.If, however, the report is routed to a disk or tape device, the control

are included in the output data.

LINES=ANSI specification works in conjunction with any HEADERs or TRAILERs

have specified.If you specify HEADER2, the ANSI specification affects this header

follows:

After HEADER1 is output, the first logical page begins with the first line of

.

logical page ends when data with a 1 in the first byte is encountered.The printing

a data record beginning with a 1 is delayed until after TRAILER2 and http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aHEADER2,

specified, are output.When record printing resumes, this delayed record will be

to have a control character  , which causes it to print over the last line of

(or HEADER3, if HEADER3 appears at the top of the page).To prevent

data record from printing over a text line of a header, the header should end with

least one blank line, specified by a slash (/).

print HEADER2 at the top of a new physical page, the HEADER2's first line

begin with a 1.

you are in complete control of the paging with LINES=ANSI, you can permit

to appear between variable numbers of printed records.

=(ANSI,n)

LINES=(ANSI,n) is specified, ANSI control characters govern vertical control, and the

'n' specification provides additional automatic paging.Added flexibility is provided be-

the user can elhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aect to double or triple space the output and still use automatic pag-

.

SyncSort encounters a data record with a 1 in the first byte, SyncSort begins a new

page.If no data record begins with a 1 but the next data record would cause the

.70 Programmer'sGuide

OUTFIL

of lines on the page to exceed n, SyncSort treats the record as if it began with a1 and begins a new page.

to the LINES=ANSI discussion for information on using a HEADER2 with ANSIcontrol characters.

OUTREC may not be used with LINES=ANSI or LINES=(ANSI,n).

ANSI Control Characters

following chart lists the ANSI control characters accepted by SyncSort.

-

InterpretationSpace one line before printingSpace two lines before printingSpace three lines before printinghttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSuppress space before printingSkip to channel 1 before printingSkip to channel 2 before printingSkip to channel 3 before printingSkip to channel 4 before printingSkip to channel 5 before printing

.Code6789ABCVWInterpretationSkip to channel 6 before printingSkip to channel 7 before printingSkip to channel 8 before printingSkip to channel 9 before printingSkip to channel 10 before print-ingSkip to channel 11 before print-ingSkip to channel 12 before print-ingSelect stacker 1Select stacker 2ANSI Control Character ChartNODETAIL Parameter (Optional)

NODETAIL parameter instructs the SortWriter facility to generate an output reportconsisting only of header and trailer entries.Data records are not included in the outputreport when this parameter is specified.

, for example, it is possible to generate a report with section trailers containing totalsand record counts without printing any data records.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparChapter 2. SyncSort Control Statements2.71

OUTFIL

OUTFIL Control Statements

following example illustrates how to use the OUTFIL control statement to definemultiple output files.OUTFIL FILES=1,OUTREC=(10:1,20,40:45,5,50:60,8),

=(21,2,CH,EQ,C'NY')

FILES=2,OUTREC=(20:1,20,50:60,8),

=(21,2,CH,EQ,C'MA')

.Sample OUTFIL Control Statement

two OUTFIL statements illustrated above are required to create two different outputfiles.

The output records in the first file (SORTOF1) contain three fields from the input

:the first input record field begins in byte 1 and is 20 bytes long, the second

record field begins in byte 45 and is 5 bytes long, and the third input record

begins in byte 60 and is 8 bytes long.This file will include only those records

'NY' in bytes 21 and 22 of the inputhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a record.These three fields will begin in bytes

, 40 and 50 of the output record.

output records in the second file (SORTOF2) contain two fields from the input

:the first input record field begins in byte 1 and is 20 bytes long, and the

input field begins in byte 60 and is 8 bytes long.This file will include only

records with 'MA' in bytes 21 and 22 of the input record.These two fields will

bytes 20 and 50 of the output record.

FILES=(01,02,03),OUTREC=(1:1,40,50:41,40)

.Sample OUTFIL Control Statement

OUTFIL statement creates three identically formatted output files: SORTOF01,SORTOF02 and SORTOF03.These files may be written to the same output device or tothree different output devices.

The output records contain two input record fields.The first input record field begins

column 1.This field began in pohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asition 1 before OUTREC processing and is 40 bytes

.The second input record field begins in column 50.This field began in position

before OUTREC processing and is 40 bytes long.The two fields will begin in po-

1 and 50 after OUTREC has been processed.

.72 Programmer'sGuide

OUTFIL

examples illustrating the SortWriter facility and the multiple output ca-

of the OUTFIL statement are provided in “Chapter 3.How to Use SyncSort's

Utility Features”.

2. SyncSort Control Statements2.73

OUTREC

Control Statement

OUTREC control statement reformats the output http://www.wendangwang.come the OUTREC state-

to accomplish the following tasks.

Delete or repeat segments of the input records.Insert character strings between data fields.Insehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art binary zeros.Create a sequence number field.Convert numeric data to printable format or to another numeric data format.Perform arithmetic operations (multiply, divide, add, subtract) and minimum and

functions with numeric fields and constants.This &quot;horizontal arithmetic&quot;

complements the &quot;vertical arithmetic&quot; already available with SUM and

TOTAL, MIN, MAX and AVG.

data to printable hexadecimal format.

, realign, and reorder data fields.

a variable length record input file to a fixed length record output file.

OUTREC parameter of the OUTFIL control statement can also be used to accomplish

of the above tasks.The INREC control statement can also be used to accomplish any

the above tasks except for converting a variable length file to a fixed length record file.

these guidelineshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a when deciding whether to use the INREC statement, the

statement, or the OUTREC parameter of the OUTFIL control statement:

Use the INREC statement to delete irrelevant data fields, reformat numeric fields to

shorter length or combine numeric fields with arithmetic operations and functions.

the size of the input records before they are sorted or merged usually im-

performance.

either the OUTREC statement or the OUTREC parameter of the OUTFIL

to expand the data record, create new numeric fields, realign data fields,

and edit numeric data, and change from variable length format to fixed

format when you are creating one output file.

the OUTREC statement when you are creating multiple output files with the

output record formatting.

the OUTREC parameter of the OUTFIL statement when you arhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae creating mul-

output files with different output record formatting.

the OUTREC statement if you need to convert a numeric field to printable format

it can be displayed in an OUTFIL header.

.74 Programmer'sGuide

OUTREC

Use the OUTREC parameter of the OUTFIL statement when an E35 exit must

the records first.

the OUTREC parameter of the OUTFIL statement when you specify the TOTAL

/or SUBTOTAL subparameters of the TRAILER parameter so that the

(s) can sum numeric fields before they have been converted to readable

and edited.

Control Statement Format

format for the OUTREC control statement is illustrated below.OUTREC FIELDS=(field1[,field2]...) [,CONVERT]

can be specified as follows:

[ c: ]

p,l [ ,subparameters]     p[ ,l ] [ ,HEX ] http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a    [ n ] X     [ n ] X'hhhh..hh'     [ n ] C'literal string'     [ n ] Z           SEQNUM,l,f [,START =  ][,INCR=  ]     n    i

.OUTREC Control Statement Format

:The n/ entry cannot be used with the INREC or OUTREC Control Statement.Itcan only be used with OUTREC parameter of the OUTFIL control statement.For a de-scription of the / entry, see “OUTREC Parameter (Optional)” on page 2.54.

Parameter (Required)

FIELDS parameter specifies fields to be included in the output record.Fields canbe data fields, spaces, hexadecimal digits, literal strings or binary zeros.

data field specified in the FIELDS parameter is identified by its position p andlength l.

:The column value (optional) specifies the output column in which

field should begin.

2. SyncSort Control Statements2.75

OUTREC

INREC, the position value indicates the fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1airst byte of the field

to the beginning of the input record after E15 processing,

specified, has completed.For OUTREC, the position value in-

the first byte of the field after E15 and INREC processing,

specified, have completed.If the OUTREC parameter of the

statement is used, the position value refers to the record

E35 processing as well.The field must begin on a byte

.

length value indicates the length of the field.The length must

an integer number of bytes.l

(X), hexadecimal digits (X'hhhh...hh'), literal strings (C'literal string') and binary

(Z) can also be specified in the FIELDS parameter.Each of these entries can be

by an 'n' value which indicates that a specified number of spaces, hex digits, li-

strings or binary zeros be inserted in the output record.Addhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aitionally, SEQNUM can

specified to place a sequence number field in the output record.

the nX entry to specify a number n of spaces.The n value

be any number from 1 to 4095 inclusive.The X entry re-

a space and must be coded to the immediate right of the

specified for n.If more than 4095 spaces are desired, two

more nX values should be specified.

the nX'hhhh..hh' entry to specify that n copies of hex-digits

hex-digit strings be inserted in the output record.(Each hh pair

1 byte of output.)The repetition factor n may be any number

1 to 4095 inclusive.

the nC'literal string' entry to specify that n copies of literal

be inserted in the output record.The repetition factor

may be any number between 1 and 4095 inclusive.An apostro-

within a literal string must be specified ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as double apostrophe;

example, C'O''LEARY'.

the nZ entry to define a specified number n of binary zeros to

inserted in the output record. The repetition factor n may be

number between 1 and 4095 inclusive.The Z entry must be

to the immediate right of n.

SEQNUM to create a sequence number field within the output

.The length of the field can be from 1 to 16 bytes and can

represented in either BI, PD or ZD formats.In addition, a

value and an increment can be specified for the field.

following describes the SEQNUM variables and parameters:

the length in bytes of the field to be created.

value from 1 to 16 can be specified.nX'hhhh..hh'nC'literalstring'nZSEQNUM

.76 Programmer'sGuide

OUTREC

the format of the field to be created.BI, PD

ZD can be specifiehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad to create either an unsigned bi-

field, a packed decimal field or zoned decimal field,

.

specifies a starting number n for the field.

n value can be 0 through 2,147,483,647.The de-

is 1.

specifies a value i that indicates how se-

numbers should be incremented.The i value

be 1 through 65,535.The default is 1.STARTINCR

maximum sequence number generated is limited to 15 deci-

digits or the length of the output field.If a number is reached

would exceed the limit, SyncSort will truncate the high order

, issue an informational message, and continue processing.

, sequence numbers will cycle within the limit.For example,

the output field is 2-bytes, then 99 will be the highest sequence

.The next number, 100, will have its high order digit

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1artruncated.The resulting number, 00, starts a new sequence

cycle from 00 to 99, regardless of the START value.

the FIELDS Parameter for Variable-Length Records

you are not using the CONVERT option to convert variable length records to fixedlength records, you must observe these rules when you specify the FIELDS parameter forvariable length records:

Remember to specify 4 bytes for the Record Descriptor Word in the first output field.

can include the 4 bytes in the length value of the first field if the first field in the

data record is also the first field specified in the FIELDS parameter.

least one byte from the fixed portion of the input records must be specified in the

parameter.

include any portion of the variable part of the input records, specify a position

without a length value as the last entry.Do nothttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a specify any other subparam-

after the position value unless HEX conversion is also specified.(Refer to the

subparameters for an explanation of HEX conversion.)

INREC or OUTREC processing changes the output record length, the contents of

Record Descriptor Word will be automatically revised by the sort.

2. SyncSort Control Statements2.77

OUTREC

Subparameters

the FIELDS subparameters to accomplish these tasks:

Specify the column in which a field should begin.Specify halfword, fullword or doubleword alignment.Convert a numeric field to a printable format with editing capabilities.Convert numeric data to another numeric data format.Perform minimum and maximum functions and arithmetic operations (multiply, di-

, add, subtract) with numeric fields and constants.

a field http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ato its printable hexadecimal representation.

chart below illustrates how the FIELDS subparameters should be specified and de-scribes their functions.For information on the EDIT, LENGTH, Mm and SIGNS subpa-rameters, see “How to Convert Numeric Data” on page 2.82.   fo                       expression ,          [ ,LENGTH=n ]           EDIT=(pattern)   [,SIGNS=(s1,s2,s3,s4)]          [ c: ]            a     p,l  ,            CHANGE=(........) [,NOMATCH=(....)]              p [,l] [,HEX]

.Fields Subparameters Format

following describes the c: subparameter:

:Use the c: subparameter to define the column in which the field should begin.

will add the appropriate number of blanks to achieve the proper align-

.This subparameter can be specified for all types of fields.

term expression represents the following syntax:

.78 Programmer'sGuide

Ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aUTREC    p,l,fi     n    -n    [ ( ]&quot;expression1&quot; [,&quot;operator&quot;,&quot;expression2&quot; ] [ ) ]

.Syntax for expression

following describes the elements of expression:

,l,fi

nThis specifies the position, length and format of an input field.(Seethe description of fi, below, for details.)This represents a positive numerical constant of up to 15 decimal

.The   sign must be specified.

represents a negative numerical constant of up to 15 decimal

.The - sign must be specified.

expression defines a numeric value.The simplest forms of an

consist of a numeric data input field defined either by

,l,fi or a constant defined by  n or -n.Expressions can also be

by connecting these simple expressions with operators, as

in the last line of the above syntax chart.Parentheses mayhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

used to change the default precedence order of the operators.

equations can thus be represented with an expression.

maximum value of 15 digits is permitted at all times in evaluating

expression.If this is exceeded, a critical error will be issued.

, an attempted divide by zero will also result in a critical

.The results of division will be rounded down to an integer.

an expression has been defined, its value can either be con-

to a numeric output data format or to a printable numeric

using editing masks.See “How to Convert Numeric Data”

page 2.82.The default is to use the M0 editing mask to create

output.The number of digits in an expression is defined

be 15 (unless the expression is a simple p,l,fi field), so using the

default mask will create a 16-byte output field.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparThe following are expressions:

10

,2,Y2Z

10,ADD,10,2,Y2Z

2. SyncSort Control Statements2.79-nexpression

OUTREC

,4,ZD

,2,PD

30

,4,ZD,ADD,10,2,PD

30,MUL,(1,4,ZD,ADD,10,2,PD)

.80 Programmer'sGuide 30,MUL,(1,4,ZD,ADD,10,2,PD),MIN,(5,5,ZD,DIV, 100)( 30,MUL,(1,4,ZD,ADD,10,2,PD)),MIN,(5,5,ZD,DIV, 100)Operations between two numeric fields or constants are performedwith operators.There are two types of operators:function operatorsand arithmetic operators.The following are the function operators:MINGenerates the minimum arithmetic value of two specifiedfields.MAXGenerates the maximum arithmetic value of two specifiedfields.The following are the arithmetic operators:MUL multiplicationDIV divisionADD additionSUB subtractionThe following rules of arithmetic precedence apply in computing an&quot;expression&quot;: Conditihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aons within parentheses are evaluated first, from inner-most to outermost parentheses. The arithmetic functions of minimum and maximum (MIN andMAX) are performed before the arithmetic operators (MUL,DIV, ADD, SUB).Within the arithmetic operators, multipli-cation (MUL) and division (DIV) are performed before addition(ADD) and subtraction (SUB).Operations within the sameprecedence level are performed from left to http://www.wendangwang.come this parameter together with p,l to define the input format ofa numeric field that is part or all of an expression.The expressionwill then be converted to either another numeric data format or toa printable format.In such cases, indicate the format of the datafield that is to be converted by replacing fi with BI, FI, PD, ZD,CSF/FS, PD0 or one of the year data formats Y2B, Y2C, Y2D, Y2P,Y2S, Y2Z.

OUTREC

use this parameter when a 2-digit packed decimal year value

to be http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aexpanded to a 4-digit packed decimal value.In such cases

fi. with Y2ID or Y2IP.The Y2ID and Y2IP formats cannot

used to form complex arithmetic expressions and do not allow the

of mask (Mm), EDIT, SIGNS or LENGTH.

l value indicating the length of the field must be specified in ac-

with the following allowable values:

BI ... 1-4 inclusive

CSF or FS... 1-16 inclusive (15 digit limit)

FI ... 1-4 inclusive

PD ... 1-8 inclusive

PD0 ... 2-8 inclusive

Y2B ... 1

Y2C ... 2

Y2D ... 1

Y2ID ... 1

Y2IP ... 2

Y2P ... 2

Y2S ... 2

Y2Z ... 2

ZD ... 1-15 inclusive

conversion of a single p,l,fi.expression with a format of Y2B,

C, Y2D, Y2P, Y2S, Y2Z, Y2ID or Y2IP does not default to the use

the M0 http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adefault output mask.The default is to convert to a 4-digit

-byte printable year.However, except for Y2S, Y2ID and Y2IP,

formats can be used to form expressions with operators.In

case, the default will be to use the M0 output mask with 15

digits.The specification of an output numeric data format

or mask Mm, EDIT, SIGNS or LENGTH is permitted except when

Y2S, Y2ID and Y2IP.

following describes the other FIELDS subparameters:

this parameter to define the output numeric data format of an

.When fo is specified, mask Mm, EDIT, and SIGNS can-

be specified.Indicate the desired format of the output field by

fo with BI, CSF/FS, FI, PD or ZD.See “How to Convert

Data” on page 2.82 for the default lengths of these fields.

“The LENGTH=n Subparameter” on page 2.87 for how this de-://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1armay be changed.

the Mm subparameter to indicate that one of the 26

-provided editing masks, M0 - M25, is to be used. Replace

'm' with the mask number.For details, see “The Mm Subparameter

(Editing Masks)” on page 2.88.Mm

2. SyncSort Control Statements2.81

OUTREC

=(pattern)Use the EDIT subparameter to specify that a user-provided editing

be used to format the output fields. For details, see “The EDIT

” on page 2.86.

=(s1,s2,s3,s4)Use the SIGNS subparameter to specify the signs that will appear

or after the edited number.For details, see “The SIGNS

” on page 2.90.

=nUse the LENGTH subparameter to alter the length of the output

.This is normally determined by the number of numeric digits

and either the data format or the edit pattern and formhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aat of the

field.For details, see “The LENGTH=n Subparameter” on

2.87.

this subparameter to tell SyncSort how the field should be

with respect to the start of the output record. Replace a with

, F or D to specify halfword (H), fullword (F) or doubleword (D)

.The alignment itself actually takes place after the col-

designation. It will automatically pad any provided field with

number of bytes of binary zeros required to achieve the specified

. This subparameter cannot be used in conjunction with

conversion.

variable represents the CHANGE subparameter.The

subparameter changes an input field to a replacement

in the reformatted output record if the input field equals

search constant.For a complete description, see “The CHANGE

” on page 2.92.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arthe HEX subparameter to convert a record field to its

representation. Specify this subparameter immediately

the position p and the length l of the field to be converted.

p,l,HEX for both fixed length records and the fixed length

of variable length records. Specify p,HEX for the variable

portion of variable length records. Starting in position p of

input record, for a length of l, each byte will be converted to its

representation.Note that in the reformatted record,

converted field will be twice the length of the original field.achange-parmHEX

to Convert Numeric Data

of the most important functions of OUTREC processing is to convert a numeric datafield or an expression to either an output numeric data format or a printable format withediting capabilities.

processing can alshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ao expand a packed decimal 2-digit year to a packed decimal4-digit year.In such cases, Y2ID or Y2IP formats are used to convert from a 2-digit to a4-digit year while maintaining a packed format.For details on converting year data, see

.82 Programmer'sGuide

OUTREC

“Converting Year Data with Century Window Processing on INREC, OUTREC or

OUTREC” on page 2.84.

a single numeric field defined by p,l,fi is to be converted, the format and length of

field determines the length of the output field, as illustrated in the chart below.

Conversion

Format

, FI

, FI

, FI

, FINumber of Bytesin Input Fieldnn1234Number of ResultingDigits (d)n2n-135810

(to maximum of 15,

truncated)

n-2 digits

digits

digits

bytes

bytesCSF or FSnPD0Y2C, Y2P, Y2http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aS, Y2ZY2B, Y2DY2IDY2IPn2112

.Data Conversion Table

any other type of expression is to be converted, the number of resulting digits d

be 15.d will be used to determine the default length of the output field, which mayChapter 2. SyncSort Control Statements2.83

OUTREC

a numeric data field (see Table12 on page 2.84) or printable output (see Table14 on

2.89).

you specify no other FIELDS subparameters, the result will be converted to printable

according to the default editing mask, M0.(Refer to “The Mm Subparameter

(Editing Masks)” on page 2.88.)Other forms of printable output can be created by using

EDIT, LENGTH, Mm and SIGNS subparameters, which allow you to create your own

patterns, or by using one of the 26 SyncSort-supplied editing masks, which are ap-

for many editing operations.

convhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aert to a numeric data field, simply specify an output format of BI, CSF/FS,FI,

or ZD.The default output field length is determined by the following table, where d

the second column represents the number of digits in the field.

Format

Length (bytes)4d   14d   1d/2   1d

.Output Length of Output Formats

lengths can be overridden by specifying the LENGTH parameter.

following five sections describe the data conversion capabilities:

Converting Year Data with Century Window Processing on INREC, OUTREC or

OUTREC

EDIT Subparameter

LENGTH=n Subparameter

Mm Subparameter (Editing Masks)

SIGNS Subparameter

.84 Programmer'sGuide

OUTREC

Year Data with Century Window Processing on INREC, OUTRECor OUTFhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aIL OUTREC

2-digit year field, as specified by the Y2B, Y2C, Y2D, Y2P, Y2S, Y2Z, Y2ID and Y2IPformats, can be converted on output to a 4-digit year:

The Y2B format specifies 2-digit, 1-byte binary year data that will be converted to a

-digit, displayable character format with the appropriate century value.For infor-

on the range of binary values representing year data with Y2B, see Table16

page 2.112.

Y2C and Y2Z formats specify 2-digit year data that is in displayable (zoned

) format.The 2-digit year data will be expanded to a 4-digit field containing

appropriate century value.

Y2S format is equivalent to Y2C and Y2Z for valid numeric year data.All three

will convert such data to a displayable 4-digit year with the appropriate

value.Y2S, however, provides additional functionality.For data with binary

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1azeros (X'00'), a blank (X'40') or binary ones (X'FF') in the first byte, typically to iden-

header/trailer records, Y2S will expand the data to 4 bytes, padded in the first 2

with the same character as found in the first byte of the input field.The fourth

of the output field is copied unchanged from the second byte of the input field.

following symbolic representation shows the treatment in hexadecimal of the

types of data:

ab

ab

OUTRECOutput000000ab404040abFFFFFFab  The Y2D and Y2P formats specify 2-digit year values in packed decimal format.The

applied to these fields will create a 4-digit year value converted to a dis-

character format.

Y2ID and Y2IP formats take as input the same 2-digit packed decimal year data

the Y2D and Y2P formats but produce a 4-digit http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ayear output that remains in packed

format.Y2ID will convert data from X'yy' to X'ccyy', and Y2IP will convert

from X'ayys' to X'accyys', where cc is the correct century.(For a description of

D and Y2P formats for SORT or MERGE processing, see Table16 on page 2.112

Table8 on page 2.37, respectively.)

that an additional data format, PD0, which is typically used to process the monthand day portion of packed decimal data, is not affected by CENTWIN processing and willnot convert 2-digit year data to 4-digit years.PD0 can be used with the SyncSort-suppliededit mask M11.The year data formats Y2B, Y2C, Y2D, Y2P and Y2Z can also be usedwhen forming expressions.The 4-digit year will be converted to an integer for arithmeticcalculations.Any expression with these formats can also be converted to an output nu-

2. SyncSort Control Statements2.85

OUTREC

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aical data format fo, or to printable output by specifying one or more of the OUTRECFIELDS subparameters (Mm, EDIT, SIGNS or LENGTH).For information on using theyear data formats for SORT or MERGE field specifications, see “CENTWIN Parameter(Optional)” on page 2.111 or “CENTWIN Parameter (Optional)” on page 2.36, respectively.For more information on using the year data formats for INREC or OUTREC processing,see “Sample OUTREC Control Statements with CENTWIN Processing” on page 2.98.

EDIT Subparameter

EDIT subparameter lets you create your own edit patterns for converted numericdata.An edit pattern can consist of:

Significant digit selectors.Leading insignificant digit selectors.Sign replacement characters.Any other characters to be printed in the actual output.

edit pattern can be up to 22 characters in length, with a maximum of 15 leading in-significant and/or signhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aificant digits.

characters used to represent significant or insignificant digit selectors are determinedby the keyword EDIT.If EDIT is specified, the letter I represents leading insignificantdigits which will print as blanks if the digits are zeros, and the letter T represents sig-nificant digits (digits that will print in their true form, even as leading zeros).

keyword EDIT can be specified with replacements for the letters I and/or T.Anyprintable character can be used as a replacement character.This replacement makesavailable to the user a pattern which encompasses all printable characters.

figure below illustrates the concept of replacing the insignificant and significant digitselectors I and T with other characters. EDxy=

: x = insignificant digit selector

=significant digit selector

.Replacing Digit Selector Characters

a blank, quotation mark or http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aunbalanced parenthesis appears within an EDIT pat-tern, the entire pattern must be enclosed within single quotation marks.Balanced pa-rentheses need not be enclosed within quotation marks.A single quotation mark withinthe pattern (i.e., an apostrophe) must be specified as two apostrophes.

.86 Programmer'sGuide

OUTREC

other characters are printed as specified in the edit pattern, with the following ex-ceptions:

Any character specified after the first leading insignificant digit selector and before

first significant digit selector will print as a blank, unless a previously selecteddigit was non-zero.

character specified after the last significant digit selector will print as a blankif the edited number is positive.

character or character string specified before the first leading insignificant digitselector, including a leading sign character, will print to the immedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aiate left of the firstsignificant digit.The appropriate number of leading blanks will be supplied, assuringthat the total number of characters in the printed field corresponds to the totalnumber of characters in the edit pattern.

leading insignificant digit selector specified after the first significant digit se-lector will be treated as a significant digit selector.

sign replacement character appearing as the first and/or last character of thepattern is replaced as per the SIGNS subparameter.

LENGTH=n Subparameter

the LENGTH=n subparameter to alter the default length of the output field data: When an editing mask is used, the default length is determined by the edit pattern

the format of the field.If LENGTH=n is not specified, the length is equal to thenumber of characters specified in the edit pattern.If LENGTH=n is specified, theedit pattern will either be truncated on thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe left or padded with blanks on the left sothat the length of the pattern equals the n value.

maximum value which can be specified for n when editing masks are used is 22. When an output data format fo is used, the default length is 4 for BI and FI formats,

is determined by the number of digits in the input expression for CFS/FS, PDand ZD formats.(The number of digits is 15 for any input expression other than asingle p,l,fi field.)If LENGTH=n is specified, the output data will either be truncatedon the left or padded on the left with zeros (or blanks for CSF/FS) of the appropriateformat to a length of n.

following are the maximum values that can be specified for n when an outputdata format fo is used:

2. SyncSort Control Statements2.87

OUTREC

Format

of n441616815

.Maximum Valhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aues of

=n for Output DataThe Mm Subparameter (Editing Masks)

MVS provides editing masks to simplify the more common editing operations.If neither Mm nor EDIT is specified in the OUTREC control statement, the default mask,M0, is used.

.88 Programmer'sGuide

OUTREC

PatternIIIIIIIIIIIIIITSTTTTTTTTTTTTTTTSI,III,III,III,IIT.TTSI,III,III,III,IIT.TTCRSI,III,III,III,IIT.TTSI,III,III,III,IIT.TTSIII-TTT-TTTTTTT-TT-TTTTIT:TT:TTIT/TT/TTIIIIIIIIIIIIIITTTTTTTTTTTTTTTTSIII,III,III,III,IITSIII.III.III.III.IITSIII III III III IITSIII III III III IITSSIII III III III IITSIII'III'III'III'IITSI,III,III,III,IIT.TTSI.III.III.IIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aI.IIT,TTSI III III III IIT,TTSI III III III IIT,TTSSI III III III IIT,TTSI'III'III'III'IIT.TTSI'III'III'III'IIT,TTSIIIIIIIIIIIIIITSigns(,,' ',-)(,,' ',-)(,,' ',-)d 1d 1Lengthd 1   [d/3]d 2   [d/3]( ,-)(' ',(,' ',))d 1   [d/3]d 2   [d/3]121188dd(' ',-)(' ',-)(' ',(,' ',))(,,' ',-)(' ',-)(' ',-)(' ',-)(' ',-)(' ',(,' ',))(,,' ',-)(' ',-)(' ',-)(' ',-)(' ',-)d 1   [(d-1)/3]d 1   [(d-1)/3]d 2   [(d-1)/3]d 1   [(d-1)/3]d 1   [(d-1)/3]d 1   [(d-1)/3]d 1   [d/3]d 1   [d/3]d 2   [d/3]d 1   [d/3]d 1   [d/3]d 1   [d/3]d 1   [d/3]d 1

14.EditingMasksChapter 2. SyncSort Control Statements2.89

OUTREC

:

M0 is the default maskThe letter d represents the number of resulting digits after data conversion.The

patterns in the Pattern column show the maximum number of resulting digits,which is 15.(Refer to Table11 on page 2.83.)

bracket symbols indicate that only the integer part http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aof this division should beretained.

Editing Masks table illustrates the following for each of the available masks.

Editpattern.Leading or trailing signs, where appropriate.Length. If a SyncSort editing mask is used for totaled or subtotaled data, the length

the output field is determined by the maximum permissible length of the dataformat, not by the specified length of the input field. The subparameter LENGTH canbe used to override the length of the output field.

edit patterns use the same symbolic letters used in the EDIT subparameter.Leadinginsignificant digits are represented by the letter I; significant digits are represented bythe letter T.Leading or trailing sign replacement characters are represented by the letterS.All other characters print as they appear in the pattern.

SIGNS illustrated for each mask follow the format requirements of the SIGNS sub-parameter.Yohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1au can specify the SIGNS subparameter to selectively override the signs fora particular mask.For example, if you specify mask M4 and also specify SIGNS=(' '), aleading blank will print instead of a plus sign if the number is positive.However, aleading minus sign will print if the number is negative because the leading negative signspecified in the editing mask has not been overridden.

lengths in the table represent the length, in bytes, of the mask.The lengths of masksM0 - M5andM10-M25aredetermined,inpart,bythenumberofdigitsd.RefertoTable11 on page 2.83 to determine the number of digits for each type of numeric field.

SIGNS Subparameter

SIGNS subparameter specifies the sign(s) that will appear before or after the editednumber.

sign replacement character, normally 'S', has special meaning if it appears as the firstor last character in an edit pattern.In these positions, the sign replacementhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a characterwill be replaced, as appropriate, by the characters specified by the SIGNS subparameter.

.90 Programmer'sGuide

OUTREC

format of the SIGNS subparameter is illustrated below. SIGNS=(s1,s2,s3,s4)

:

= leading positive sign indicator

= leading negative sign indicator

= trailing positive sign indicator

= trailing negative sign indicator

the SIGNS subparameter contains four positional values, commas must be usedto indicate embedded, unspecified values.Each of the four values can contain one, andonly one, character; specified characters must be separated by commas.

blank, comma, quotation mark and unbalanced parenthesis used as a SIGNS charactermust be enclosed within apostrophes.An apostrophe used as a SIGNS character mustbe specified as two apostrophes enclosed within apostrophes ('''').

the SIGNS subparameter is spechttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aified, the letter 'S' is normally used as the signreplacement character in the user-supplied edit pattern.The user can change the lastletter of the keyword SIGNS in order to specify another character as the sign replacementcharacter.For example, if the user specifies SIGNX instead of SIGNS, the letter 'X' be-comes the sign replacement character in the user-provided edit pattern.

the user specifies a sign replacement character in the edit pattern but does not specifya value in the corresponding position in the SIGNS parameter, a blank will be assumed.For example, if the user specifies the following:

=(IITT.TTS),SIGNS=(,,,-)

a trailing minus sign will print if the number is negative and a trailing blank willprint if the number is positive.

SIGNS subparameter can also be used to override the sign values inSyncSort-provided editing masks.

2. SyncSort Control Statements2.91

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparOUTREC

CHANGE Subparameter

CHANGE subparameter changes an input field to a replacement constant in the re-formatted output record if the input field equals a search constant.The input field re-mains unchanged on the input side.

format of the CHANGE subparameter is shown below:[c:] p,l,CHANGE=(o,srch1,repl1 [,srch2,repl2 ... srchn,repln])

nmrepl    ,NOMATCH=(    )     r,n

43.ChangeSubparameter

search-replacement paired constants, with different data formats, can be speci-fied on a CHANGE subparameter.Note the following rules for mixing data formats: Search constants are character, hexadecimal, or binary strings.Multiple search

on a CHANGE subparameter can be a mixture of character andhexadecimal formats.Binary search constants cannot be mixed with search con-stants of other formats; thus, if one search constant on a CHANGE subparameter ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asbinary, all other search constants on that subparameter must also be binary.

constants are character or hexadecimal strings.Multiple replacementconstants on a CHANGE subparameter can be a mixture of character andhexadecimal data formats.

constants of a search-replacement pair can be of different data format.For ex-ample, a hexadecimal or binary search constant could be paired with a character re-placement constant, or a character search constant could be paired with ahexadecimal replacement constant.Thus, you could change a hexadecimal or binaryinput field to a character output field, or you could change a character input field toa hexadecimal output field.

following describes the elements of the CHANGE subparameter:

,lThe normal SyncSort position-length designation that specifies the input

. When this field matches a search constant, the field will be changed

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an the output to a replacement constant.

character or hexadecimal search constants, the input field can be 1

64 bytes long.For binary search constants, the input field must be one

.

.92 Programmer'sGuide

o

,n OUTREC The length of the output replacement field. Permissible length is 1 to 64bytes.The search constant to which the input field is compared.Permissibleformats are character string (C'x...x'), hexadecimal string (X'x...x'), or abinary byte (B'bbbbbbbb').When the search constant matches the inputfield, the input field will be changed to an output replacement constant.If one of the search constants is binary in a set of search-replacementpairs on a CHANGE subparameter, then all the search constants on thatCHANGE subparameter must be binary.(For additional information onusing binary fields in INCLUDE/OMIT processing, seehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a “INCLUDE/OMITControl Statement” on page 2.16.)If the search constant is longer than the length l of the input field, theconstant will be truncated to length l.If the search constant is shorterthan l, the constant will be padded on the right to length l.Characterstrings are padded with blanks (X'40').Hexadecimal strings are paddedwith zeros (X'00').Binary strings are neither truncated nor padded sinceonly one-byte strings are permissible.The replacement constant to which the input field is changed in the re-formatted output record when the input field matches a search constant.Permissible formats are character string (C'x...x') and hexadecimal string(X'x...x').If the replacement constant is longer than the length o of the output field,the constant will be truncated to length o.If the replacement constantis shorter than o, the constant will be padded on the right to length o.Character strings are padded with blanks (X'40').Hexadecimhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aal stringsare padded with zeros (X'00').Indicates how SyncSort should respond if the input field does not matcha search constant.If NOMATCH is not specified and no search constantmatches the input field, sort processing will terminate with an errormessage.A replacement constant to which the input field is changed in the refor-matted output record when the input field p,l fails to match a searchconstant.For details, see the description of the repl variable above.The position r and length n of an input field that will be inserted in the

record when the CHANGE input field p,l fails to match a search

.

must be at least 1.If n is greater than the length o specified for the

replacement field, the output field r,n will be truncated on the

2. SyncSort Control Statements2.93

OUTREC

to length o.If n is lessthan o, the field r,n will be padded on the

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparright with blanks (X'40') to the length o.

following example illustrates the use of the CHANGE subparameter:OUTFIL OUTREC=(16,2,

=(13,C'NJ',C'NEWJERSEY',

'NY',C'NEWYORK',

'PA',C'PENNSYLVANIA'),

=(C'NOTSUPPORTED'),

X,

,1,

=(10,B'1.......',C'EASTCOAST',

'0.......',C'WESTCOAST'))

.Sample OUTREC Parameter with CHANGE Subparameter

the above example, the OUTREC parameter contains two CHANGE subparameters.The first CHANGE subparameter changes the input field 16,2 to a state name in the re-formatted output record when the input field matches a state code.If no matches arefound, the output field will be 'NOT SUPPORTED.' The second change subparameterchanges the one-byte input field 24,1 to 'EAST COAST' or 'WEST COAST' in the refor-matted output record, depending on the binary contents of the input field.

followihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ang example illustrates a situation that can arise when using binary searchconstants.In such cases, more than one search constant may match an input field:OUTFIL OUTREC=(24,1,

=(6,B'.....11.',C'SHARE',

'......1.',C'UNIQUE'))

.CHANGE Subparameter with Binary Search Constants

that in the above example, the input field X'06' would match both binary searchconstants.In such cases, the first search constant is used, thus the output would be thecharacter string 'SHARE'.If the input field were X'02', the output would be the characterstring 'UNIQUE'.

.94 Programmer'sGuide

OUTREC

Parameter (Optional)

CONVERT parameter enables you to convert variable length records into fixed lengthrecords.

records do not require an RDW and will be written to the output file(s) with aRECFM of F or FB. When using CONVERT, you no longer need to apply the ruleshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a for&quot;Specifying the FIELDS parameter for Variable Length Records.&quot;

may create multiple output files with different record formats when specifyingCONVERT in conjunction with the OUTREC parameter on the OUTFIL control state-ment.

cannot specify the variable portion of the input records (position without length)when using CONVERT.However, all data fields need not be present in each record beingCONVERTed, unless a numeric or Y2K field is specified.That is, blanks will be used forany missing p,l field bytes, while all p,l,f fields must be present.

OUTREC Control Statements

1

following example illustrates how the OUTREC statement can be used to insert bi-nary zeros and blanks into the record. OUTRECFIELDS=(1:4Z,5:20,10,23:44,28,10X)

.Example 1, Sample OUTREC Control Statement

OUTREC statement defines a 60-byte record as follows:

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar

Four binary zeros are inserted in the first 4 bytes of the record (4Z).The next field begins in position 5.This field began in position 20 before OUTREC

and is 10 bytes long (5:20,10).

blanks are inserted before the next field, which is positioned at byte 23.SyncSort MVS automatically inserts blanks in the unused positions between fields.The next field begins in position 23.This field began in position 44 before OUTRECprocessing and is 28 bytes long (23:44,28).

blanks are inserted in the last 10 bytes of the record (10X).

2

2. SyncSort Control Statements2.95

OUTREC

following example illustrates how the OUTREC statement can be used to convert andedit numeric fields. OUTREC FIELDS=(1,50,64,4,PD,M2,68,6,ZD,

=($I,IIT.TTS),SIGNS=(,, ,-))

.Example 2, Sample OUTREC Control Statement

OUTREC statement dehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afines a 70-byte output record as follows:

The first field (1,50) begins in position 1.

processing and is 50 bytes long.This field began in position 1 before

The next field (64,4) begins in position 51.This packed decimal field began in posi-

64 before OUTREC processing and is 4 bytes long.After being converted andedited by editing mask M2 (64,4,PD,M2) the resulting field will be 10 bytes long.However, the number of digits that will actually print will depend on the number ofleading zeros, if any, because this mask specifies that only three digits must printwhether or not they are leading zeros.Moreover,this mask specifies that a minussign print after the number if it is negative and a blank print after the number if itis positive.

last field (68,6) begins in position 61.This zoned decimal field began in position68 before OUTREC processing and is 6 bytes long.The EDIT and SIGNS suhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1abpa-rameters (EDIT=($I,IIT.TTS),SIGNS=(,, ,-)) specify a 10-byte field because 4 addi-tional bytes are needed for the dollar sign, the comma, the decimal point and thetrailing plus or minus sign.Note that if the first three digits are leading zeros, theywill be suppressed.

3

example uses the OUTREC statement to convert numeric data from one format toanother. OUTREC FIELDS=(1,10,ZD,PD,

,4,FI,ZD,LENGTH=8)

.Example 3, Sample OUTREC Control Statement

OUTREC statement defines a 14-byte output record as follows:

The first field (1,10,ZD,PD) begins in position 1.This field was a 10-byte ZD field

began in position 1 before OUTREC processing.It will be converted to a 6-byte

.96 Programmer'sGuide

OUTREC

field in the output record, because 6 bytes are required to contain 10 decimaldigits as a PD field.

The next field (11,4,FIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,ZD) begins in position 7.This field was a 4-byte FI field that

in position 11 before OUTREC processing.It will be converted to an 8-byteZD field in the output record.Normally 10 ZD bytes would be required to contain the10 decimal digits that may be represented by a 4-byte FI field, but the LENGTH=8parameter overrode the output length.If there are more than 8 decimal digits in anyof the 11,4,FI fields, those digits will be truncated on the left in the output record.Note that ZD output is not the same as printable output using editing masks.Highorder zeros will appear as zeros in a ZD field, while they appear as blanks when usingthe default M0 mask, as well as most other masks.The sign indicator in a ZD fieldis placed in the first 4 bits of the rightmost byte, and not as a separate printable sign.Example 4

OUTREC example uses arithmetic and function operators to do algebraic calcu-lations.

8-byte http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPD fields are required in each record containing the maximum and averageof fields A, B and C.Another new 5-byte printable field is required containing field D asa percentage of field E.The field definitions are:

A:

B:

C:

D:

E: 1,4,PD5,8,ZD13,4,FI25,4,PD29,4,PD

OUTREC statement to accomplish this would be:

2. SyncSort Control Statements2.97

OUTREC  OUTREC FIELDS=(1,36,

:(01,4,PD,ADD,

,8,ZD,ADD,

,4,FI),

, 3,

,

*

:01,4,PD,MAX,

,8,ZD,MAX,

,4,FI,

,

*

: 100,MUL,

,4,PD,DIV,

,4,PD,

=5)

*Retain existing fieldsField A plusField B plusFieldCdivide by 3 to get averageoutput as 8-byte PD fieldDetermine maximum of Field A andField B andFieldCoutput as 8-byte PD field100timesField D divided byFieldEoutput ashttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a printable 5-byte fieldusing default M0 mask

.Example 4, Sample OUTREC Control Statement

OUTREC statement defines a 64-byte output record as follows:

The first field (1,36) retains the complete contents of the input record.The second output field begins in position 40.An arithmetic calculation is done using

different numeric input fields and the constant  3 to compute the arithmeticaverage.This is an expression that is considered to contain 15 decimal digits.Theoutput is requested as a PD field.The length of this field will be 8 bytes, since thatis the length required to contain 15 decimal digits.

third output field begins in position 50.Multiplying numeric Field D by 100before dividing by numeric Field E gives the desired percentage number, which isconsidered to contain 15 decimal digits.No output format or editing mask is speci-fied, so the default mask M0 is usehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad to create printable output.LENGTH=5 isspecified to reduce the default length of the output field from 16 to 5, since it is knownthat the percentage number will not be large.

examples illustrating the OUTREC control statement and the OUTRECparameter of the OUTFIL statement are provided in “Chapter 3.How to Use SyncSort'sData Utility Features”.

.98 Programmer'sGuide

OUTREC

OUTREC Control Statements with CENTWIN Processing

century window processing, data conversion is determined by the century windowdefined by the CENTWIN parameter.

following provides examples of data conversion with CENTWIN:

1

2-digit year field in character format at position 20 in the input record could be ex-panded with the following specification:OUTREC FIELDS=(1,19,

,2,Y2C,

,59)* Copies first 19 bytes of record* Converts 2-digit year data to 4-dhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aigit year* Copies remaining 59 bytes

.Example 1, OUTREC Control Statement with Year Data

that the expansion of the year data from 2 to 4 digits increases the output recordlength by 2 bytes compared to the input record length.

CENTWIN setting determines the century of the 2-digit year field.IfCENTWIN=1980, then a year field in the input record would be converted as follows:

OUTRECOutput2013207919801992

2

the following packed decimal date field at position 20 in the input record:yymmdd = X'0yymmddC'

you want to output a displayable 4-digit year in character format in the formmm/dd/yyyy

accomplish this, specify the following OUTREC control statement:

2. SyncSort Control Statements2.99

OUTREC OUTREC FIELDS=(1,19,

,2,PD0,M11,

'/',

,2,PD0,M11,

'/',

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar20,2,Y2P,

,76)* Copies first portion of record* Converts X'ymmd' to X'mm' then C'mm'*Insertsslash* Converts X'mddC' to X'dd'then C'dd'*Insertsslash* Converts X'0yym' to X'yy' then C'yyyy'* Copies rest of record

.Example 2, OUTREC Control Statement with Year Data

4-digit year output from the input year field (20,2,Y2P) depends on the CENTWINsetting.The following sample input and output data shows the case for CENTWIN=1980:

Input Date Field

'0800329C'

'0790603C'OUTREC Output Date Field03/29/198006/03/2079

3

expand a 3-byte packed decimal date field of the form X'yyddds', at position 20 in theinput record, to a 4-byte packed field of the form X'yyyyddds' that contains a prefixedcentury value, specify an OUTREC control statement such as the following:

FIELDS=(1,19,

,1,Y2ID,

,60)

** Copies first portion of rhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aecord* Converts X'yy' to X'yyyy'* Copies rest of record starting withthe X'ddds' of the date field

.Example 3, OUTREC Control Statement with Year Data

that in the above example the output record length will be 1 byte larger than theinput record length.The following sample input and output data shows the effect forCENTWIN=1980:

Input Date Field

'79'

'80'OUTREC Output Date FieldX'2079'X'1980'

.100 Programmer'sGuide

OUTREC

4

expand a 4-byte packed decimal date field of the form X'0yymmdds', at position 20 inthe input record, to a 5-byte field of the form X'0yyyymmdds' that contains a prefixedcentury value, specify an OUTREC control statement such as the following: OUTREC FIELDS=(1,19,

,2,Y2IP,

,59)

** Copies first portion of record* Converts X'0yym' to X'0yyyym'* Copies rest of record starting with* the X'mdds' ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1af the date field

.Example 4, OUTREC Control Statement with Year Data

with Y2ID conversion, the output record length will be 1 byte larger than the inputlength.The following sample input and output data shows the effect forCENTWIN=1980:

Input Date Field

'0790'

'0801'OUTREC Output Date FieldX'020790'X'019801'

5

a 2-byte character or zoned decimal field that may contain either valid numericyear data or characters that identify the record as a header or trailer.Header records inthe example are identified by zeros (X'00') or a blank (X'40') in the first byte of the yearfield, while trailer records are identified by binary ones (X'FF') in the first byte of the field.The Y2S format will treat the valid year data normally, in the same way as the Y2C orY2Z formats would treat the data, but the year fields of header and trailer records willbe converted to ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a 4-digit form padded on the left with data identical to the data in the firstbyte of the input field.

this type of conversion is needed when a Y2S SORT or MERGE field is used tocollate the records so that header/trailer records in the output remain at the start or endof the file.An OUTREC statement such as the following could be used.

2. SyncSort Control Statements2.101

OUTREC  OUTREC FIELDS=(1,19,* Copies first portion of record

,2,Y2S, * Converts C'yy' to C'yyyy' and pads

*fields that identify header/trailer records

,59)* Copies the remaining fields

.Example 5, OUTREC Control Statement with Year Data

with Y2C or Y2Z, the output record length will be 2 bytes larger than the input recordlength.

CENTWIN=1990, the sorted Y2S field would be converted as follows:

Input Date Field

'4001'

'F9F8'

'F0Fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a3'

'0000'

'FFFF'OUTREC Output Date FieldX'00000000' (from 4th input record)X'40404001' (from 1st input record)X'F1F9F9F8' (from 2nd input record)X'F2F0F0F3' (from 3rd input record)X'FFFFFFFF' (from 5th input record)

.102 Programmer'sGuide

RECORD

Control Statement

RECORD control statement provides record length and format information.It isrequired in the following situations:

SyncSort is invoked by a program passing either a 24-bit or 31-bit extended param-

list and using an in-memory E15 or E32 exit routine.

E15 or E35 exit routine changes the record length.

Control Statement Format

format of the RECORD control statement is illustrated below:   F  RECORD   TYPE=     [,LENGTH=(l1,l2,l3,l4,l5,l6,l7) ]   V

.RECORD Control Statement Format

Parameter (Optional)

TYPE parameter can be ushttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed to indicate the record format.TYPE=F indicates fixedlength records; TYPE=V indicates variable length records.TYPE=FB or TYPE=VB canbe specified but the 'B' is ignored.

should be specified if SORTIN is VSAM.If TYPE is not provided, the SORTOUTRECFM will be examined to determine the SORTIN TYPE.If no SORTOUT RECFM isfound, TYPE=Vwill be assumed if the SORTOUT is VSAM and TYPE=F if theSORTOUT is non-VSAM.

:If the TYPE specification differs from the RECFM DCB parameter for theSORTIN/SORTINnn DD statement, the latter takes precedence.

Parameter (Conditionally Required)

LENGTH parameter, usually optional, is required whenever the RECORD statementis required.

LENGTH parameter specifies the length of the record at various points during theprocessing of the application.

number of length values can vary from 1 to 7.Only the l1, l2 and l3 values shouldbe specified for fihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1axed length records and for merge or copy applications.All seven lengthvalues can be specified for variable length sorts.If l1 is the only value specified, paren-

2. SyncSort Control Statements2.103

RECORD

are optional.If l1 and additional length values are specified, they all must beenclosed in parentheses.

length values are positionally dependent.An extra comma must indicate a missinglength value between any two that are http://www.wendangwang.commas need not follow the final lengthvalue specified.For example, if LENGTH=(l1,,,l4) is specified, the omitted values areunderstood to be l2 and l3.

l1,...,l7 variables specify the following:

The maximum record input length of the logical records.For variable length

, this is the length of the longest logical record plus the 4-byte Record

Word.The 4-byte RDW must be included, even if the ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anput is a

file.The maximum record length cannot exceed 32,760 for fixed length

and 32,767 for variable length records.An LRECL value specified on

SORTIN/SORTINnn DD statement or the data set label will override the

value for fixed length records.For variable length records, the higher value

(LRECL or l1) is used.

maximum length of the logical records after E15 processing. An omitted

value defaults to the l1 value and indicates that the maximum record length

not been changed by an E15 exit.If there is no E15 exit, an l2 value which

smaller than the l1 value or the LRECL specified on the SORTIN/SORTINnn

statement or data set label will truncate the records.This truncation will

after the record is read from SORTIN.

maximum length of the logical records after E35 processing.If the l3

is omittedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a, the default is either the l2 value, or, if an INREC and/or

statement is specified, the record length after INREC/OUTREC

.Note that it is not necessary to specify an l3 value to reflect a

change due to INREC or OUTREC processing; the revised record length

calculated automatically.However, it is necessary to specify an l3 value if

E35 has altered the record length.

LRECL value specified in the SORTOUT DD statement should either

to the l3 value or the LRECL specification should be omitted.In

latter case, SyncSort will automatically calculate the correct LRECL value.

l3 value is ignored if there is no E35 exit, so it is not possible to use the

value to truncate or pad the records.

The minimum length of the variable length logical records plus the 4-byte Re-

Descriptor Word.An omitted l4 http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1avalue defaults to the length from the

of the record to the end of the last field referenced by any control

.

most frequent record length of the variable length records.Specify this

value to optimize the size of the segment, i.e., the fixed length block of

storage, used to contain variable length records.l2l3l5

.104 Programmer'sGuide

RECORD

The average work space required by each record, as reported by the

utility program.The l6 value will be ignored for a Tape Sort.

segment length recommended by the HISTOGRM utility program.If l7

omitted, the SIZE parameter on the SORT statement may be used to deter-

the impact of segment size on sort performance.Assuming the SIZE

reports a SORTIN data set of at least 10,000 records, SyncSort may

the first 100-200 records to http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acalculate an approximate segment size.

installation may decide to allow record sampling for smaller files.The l7

will be ignored for a Tape Sort.l7

for Specifying the Length Parameter

the following rules when specifying length values:

All length values for variable length records must include 4 bytes for the Record

Word.

l1, l2, and l3 values must represent the maximum record lengths and the l4 valuemust represent the minimum record length.If SyncSort encounters a record whichexceeds the maximum length or is shorter than the minimum length, the applicationwill either terminate abnormally or produce unpredictable results.

RECORD Control Statement RECORDTYPE=F,LENGTH=(80,,60)

.Sample RECORD Control Statement

sample RECORD statement defines the record as follows:

The file contains http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afixed length records.The input record length (l1) is 80 bytes.A comma represents the omitted l2 value because an E15 exit does not change the

length.

record length after INREC/OUTREC and/or E35 processing is 60 bytes.TheSORTOUT LRECL should either be specified as 60 or omitted.If it is omitted,SyncSort will automatically supply the correct value.

2. SyncSort Control Statements2.105

RECORD  RECORDTYPE=V,LENGTH=(400,300,250,l20,200,280,230)

.Sample RECORD Control Statement

sample RECORD statement defines the record as follows:

The file contains variable length records.All length values include 4 bytes for the

Descriptor Word.

maximum input record length is 400 bytes.

maximum record length after E15 processing is 300 bytes.

maximum record length after INREC/OUTREC and/or E35 processing is 250bytes.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arThe minimum record length is 120 bytes.

most frequent record length is 200 bytes.

average work space required for each record is 280 bytes, as reported by theHISTOGRM utility program.

segment length recommended by HISTOGRM is 230 bytes.

the above example, the l4, l5, l6 and l7 values will be ignored if the application is amerge or copy.

.106 Programmer'sGuide

SORT

Control Statement

SORT control statement defines the application as a sort or copy application.

a SORT control statement or a MERGE control statement is required for everyapplication.

Environment Support

environment support allows you to choose an alternative set of collating rulesbased on a specified national language.The alternative collating applies toSORT/MERGE and INCLUDE/OMIT processing.

additional detail, see “LOCALE” ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an page 5.21.

Control Statement Format

format of the SORT control statement is illustrated below.SORT   FIELDS=(p1,l1,f1,o1 [,p2,l2,f2,o2] ...)  FIELDS=(p1,l1,o1 [,p2,l2,o2]...),FORMAT=f FIELDS=COPY

,CKPT  ,CENTWIN=      ,CHKPT     f

,DYNALLOC                 d  (nn,mm)   =  (d, n ,RETRY=      [,SC=s])

,EQUALS      n         ,FILSZ=          En

n    ,SIZE=    [ ,SKIPREC=n ] [,STOPAFT=n ]   En

.SORT Control Statement Format

2. SyncSort Control Statements2.107

SORT

Parameter (Required)

FIELDS parameter is required.It describes the control fields.

the control fields in order of greatest to least priority, with the primary control fieldlisted first, followed by progressively less significant fields.You can specify up to 128control fields; however, if fields are http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acomplex, the limit for a particular execution may beless than 128.

field specified in the FIELDS parameter is identified by its position (p), length (l),format (f) and order (o).

position value indicates the first byte of the field relative to the beginning of

input record after INREC and/or E15 processing, if specified, have completed.Binary control fields can begin on any bit of a byte.When a binary field does notbegin on a byte boundary, you must specify the bit number (0-7).For example, aposition value of 21.3 refers to the 4th bit of the 21st byte of the record.

length value indicates the length of the control field.The length value must

an integer number of bytes except for the length of a binary control field whichcan be specified in bits.For example, a length value of 0.5 refers to a binarycontrol field 5 bits long.

signed fields, the length value must inclhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aude the area occupied by the sign.

format value indicates the data format.For a list of valid formats, refer to

table in the next section, &quot;Valid Formats for Sort Control Fields.&quot;If all thecontrol fields have the same format, you can specifythe format value once byusing the FORMAT=f subparameter. If you specify both the individual f valuesand the FORMAT subparameter, the individual f values will be used.(Note thatthe f values must be specified for each control field).

order value indicates how the field is to be collated:

A=AscendingorderD=DescendingorderE=As modified by an E61 exit.Ascending ordero

.108 Programmer'sGuide

SORT

Formats for Sort Control Fields

chart below lists the valid formats for sort control fields.Code

*

*Data FormatEBCDIC characters are translated to their ASCII equivalents beforesorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aing.Character. Records are sorted according to an alternate sequence

either in the ALTSEQ control statement or as an installation

.

separate sign. An ASCII   or - precedes numeric field.One

per byte.

separate sign. An ASCII   or - trails numeric field.One digit

byte.

. Unsigned.

. Unsigned.

overpunch sign. Hexadecimal F,C,E, or A in the first 4 bits

your field indicates a positive number. Hexadecimal D or B in the

4 bits indicates a negative number. One digit per byte.

=CLC is forced.

sign format.An optional leading sign may be specified im-

to the left of the digits.If the sign is a -, the number is

as negative.For other characters, the number is treated as

.Characters to the left of the sign are ignored.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aseparate sign. An EBCDIC   or - precedes numeric field.

digit per byte. CMP=CLC is forced.

separate sign. An EBCDIC   or - follows numeric field.One

per byte. CMP=CLC is forced.

point. Signed. (Equivalent to Signed Binary.)

point. Normalized. Signed.

decimal. Signed.

decimal.2-8-byte packed decimal data with the first digit and

sign ignored.The remaining bytes are treated as packed

digits.Typically PD0 is used with century window processing

Y2P format; Y2P processes the year, while PD0 processes month

day.Field Length(bytes)1 to 2561 to 256ASL*AST*BICHCLO*OL*2 to 2562 to 2561 bit to 4092**1 to 4092**1 to 256CSFFS1 to 16CSL*LS*CST*TS*FIFLPDPD0*2 to 2562 to 2561 to 2562 to 161 to 2562-8

2. SyncSort Control Statements2.109

SORT

B*

C*Bhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ainary. 2-digit, 1-byte binary year data treated as a 4-digit year byCENTWIN (century window) processing.Character.2-digit character year data treated as a 4-digit year by

(century window) processing.Processing is identical to

Z fields.

decimal.2-digit, 1-byte packed decimal year data treated as

4-digit year by CENTWIN (century window) processing.

decimal.2-digit, 2-byte packed decimal year data.Of the four

digits contained in the 2 bytes, the first digit and trailing sign

ignored; the two inner digits are treated as a 4-digit year by

processing.

or zoned decimal.2-digit, 2-byte valid numeric data

as a 4-digit year by CENTWIN (century window) processing,

for Y2C and Y2Z.However, certain data is not treated as year

.Data with binary zeros (X'00') or a blank (X'40') in the first bytehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

be collated before valid numeric year data for ascending order

(after year data for descending order).Data with all binary ones

(X'FF') in the first byte will be collated after valid numeric year data

ascending order (before year data for descending order).Zones are

, as for Y2C and Y2Z, except for data where the first byte be-

with X'00', X'40' or X'FF'.

decimal.2-digit, 2-byte zoned decimal year data treated as a

-digit year by CENTWIN (century window) processing.The zones

ignored.Processing is identical to Y2C fields.

decimal. Trailing overpunch in the first 4 bits of the rightmost

gives the sign. Hexadecimal F,C,E, or A indicates a positive

. Hexadecimal D or B indicates a negative number. One digit

byte. CTO forces CMP=CLC.

* Cannot be used with Tape Sort.

** 4084 for vahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ariable-length records.

.Format Code Chart12Y2D*Y2P*12Y2S*2Y2Z*2ZDCTO*OT*Note:1 to 256

information on the year data formats (Y2B, Y2C, Y2D, Y2P, Y2S and Y2Z) plus therelated data format PD0, see “CENTWIN Parameter (Optional)” on page 2.111, “Con-verting Year Data with Century Window Processing on INREC, OUTREC or OUTFILOUTREC” on page 2.84, and &quot;Specifying Field-to-Field Standard Comparisons for DateFields&quot; in the INCLUDE/OMIT Control Statement section of this chapter.

.110 Programmer'sGuide

SORT

for Specifying Sort Control Fields

For fixed length records, all control fields and the sum of their lengths cannot exceed

bytes.When EQUALS is in effect, the number is reduced 4 bytes to 4088 bytes.EXTCOUNT also reduces the number by 4 bytes.Thus, if both EQUALS andEXTCOUNT are in effect, the number is reduced to 4084 bytes.

variable length recohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ards, all control fields must be located within the first 4084bytes, and the sum of their lengths cannot exceed 4084 bytes.When EQUALS is ineffect, the mumber is reduced 4 bytes to 4080 bytes.EXTCOUNT also reduces thenumber by 4 bytes.Thus, if both EQUALS and EXTCOUNT are in effect, the numberis reduced to 4076 bytes.

fields can be in contiguous or noncontiguous locations in the record.

that for variable length records, the first 4 bytes are reserved for the Re-cord Descriptor Word, so the first byte of the data portion of the record is byte 5.

the output file is a key-sequenced VSAM cluster, the VSAM key must be the firstcontrol field specified.

PD and ZD Control Fields

CMP PARM determines how PD and ZD control fields will be compared.WhenCMP=CPD is in effect, the Compare Decimal (CP) instruction is used for the compare.ZD fields are packed and then compared.Thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahis method has performance advantages.However, invalid PD data may cause a system 0C7 abend and program termination.Moreover, the integrity of ZD fields is only guaranteed when they contain valid ZD data.The CMP=CPD method cannot be used if any control field exceeds 16 bytes, for variablelength sorts when an even value (0, 2, 4 or 6) is specified for the VLTEST PARM, or fora Tape Sort.

CMP=CLC is in effect, no data validation is performed and the integrity of theoutput is maintained, even if the sign for a PD or ZD field is invalid.This method is al-ways used for control fields that exceed 16 bytes, for variable length sorts when an evenvalue is specified for the VLTEST PARM, and for a Tape Sort.

Parameter (Optional)

CENTWIN run-time or installation option acts on 2-digit year data.CENTWINgenerates a century window (for example, 1950 through 2049) that determines the cen-tury to which a 2-digithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a year belongs.At run-time, CENTWIN can be specified as eithera PARM option or a SORT/MERGE statement parameter.CENTWIN ensures that yeardata spanning centuries will be sequenced correctly.Without CENTWIN processing, anascending sort would sequence the year 01 before the year 98.With CENTWIN process-ing, the 01 field could be recognized as a twenty-first century date (2001) and would thusbe sequenced after 98 (1998).

2. SyncSort Control Statements2.111

SORT

more information on specifying the CENTWIN option, see “CENTWIN” on page 5.8.CENTWIN SORT/MERGE processing only applies to data defined as year data formats:Y2B, Y2C, Y2D, Y2P, Y2S and Y2Z.These data formats enable SyncSort to process2-digit year fields as 4-digit years.A related data format, PD0, can be used to process themonth and day portions of packed decimal date fields.To correctly specify date fields forCENTWIN SORT processing, you shouldhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a be familiar with the CENTWIN-related dataformats.

following describes each of the year data formats and provides SORT control state-ment examples:

Y2B Format

format is used to sequence 2-digit, 1-byte binary year data with CENTWIN proc-essing.The binary values are converted to decimal, and the two low order digits are usedas year data.Thus, while binary and decimal values range from 00 to 255, year valuesrange from 00 to 99.The relationship between binary, decimal and year values is shownin the following table:

Value

'00' to X'63'

'64' to X'C7'

'C8' to X'FF'Decimal Value00 to99100 to 199200 to 255Year Value00-9900-9900-55

. Possible Values Representing Year Data

Y2BThe Y2C and Y2Z Formats

formats represent 2-digit, 2-byte year data in either character (Y2C) or zoned dec-imal (Y2Z) format.Either Y2C and Y2Z formats can be http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aused with data of the form

'xyxy'

y is a hexadecimal year digit 0-9 and x is hexadecimal 0 through F.Y2C and Y2Zignore the x digits, leaving yy, the 2-digit unsigned year representation.

you have a character or zoned decimal date field mmddyy that begins at byte 20.You can use either Y2C or Y2Z to process the yy field.As the following example indicates,you could specify three sort keys to correctly sort this date:

.112 Programmer'sGuide

SORT SORT FIELDS=(24,2,Y2C,A,

,2,CH,A,

,2,CH,A)* Sorts yy field as 4-digit year* Sorts mm field* Sorts dd field

yy field (24,2) will be processed according to the century window setting.For exam-ple, if CENTWIN=1945, the field yy=45 will be sequenced as if it were 1945, and yy=44would be sequenced as if it were 2044.Thus, for an ascending sort, 44 would follow 45.The Y2D Format

format is used to sequence 2-http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adigit, 1-byte packed decimal year data with http://www.wendangwang.come Y2D to extract the year data yy from packed decimal date fields.Forexample, consider a 3-byte packed decimal data field defined as

'yyddds'

field has the year yy in the first byte and the day ddd in bytes 2 and 3.The packeddecimal sign s would be in the last digit (half byte) of the third byte.To sort this datefield, which begins at byte 20, with 4-digit year processing, use the following SORT con-trol statement:

FIELDS=(20,1,Y2D,A,

,2,PD,A)* Sorts 2-digit year (yy) as 4-digit year* Sorts ddds as 3 digits (ddd)

Y2P Format

format is used to sequence 2-digit, 2-byte packed decimal year data with http://www.wendangwang.come Y2P to extract the year data yy from packed decimal date fields spanning2 bytes.For example, a packed decimal date of the form yymmdd would be stored as 4bytes:

= X'0http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ayymmddC'

the trailing C (sometimes F) is a positive sign and the leading 0 pads the field onthe left to make an even number of digits.

that the components of the date span bytes:

y ym md dC

2. SyncSort Control Statements2.113

SORT

P handles this condition by ignoring the first and last half bytes of the 2-byte fieldspecification.Thus, Y2P processes 0yym as yy, ignoring the leading digit 0 and thetrailing digit m that is part of the month.

following example uses Y2P to sort the year portion of the date field, which beginsat byte 20:SORT FIELDS=(20,2,Y2P,A) * Sorts yy field as 4-digit year

field specification 20,2,Y2P treats X'0yym' as X'yy', and CENTWIN processing sortsyy as a 4-digit year yyyy.

PD0 format, described below, can assist Y2P by processing month and day data thatoverlaps year data in the original field.

Y2S Fohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1armat

format is used to sequence 2-digit, 2-byte character or zoned decimal data.The Y2Sformat is identical to Y2C and Y2Z for valid numeric data, but Y2S treats data that beginswith X'00', X'40' or X'FF' as non-year data.Thus, the Y2S format can distinguish recordsthat have non-year data in the first byte of the year field, allowing such records to besorted differently from other records.

S treats non-year data as follows:

Data with binary zeros (X'00') or a blank (X'40') in the first byte will not have century

processing applied to it.Instead, such data will be collated in sequence, be-fore valid numeric year data for ascending order or after the year data for de-scending order.

with all binary ones (X'FF') in the first byte will also not have century windowprocessing applied to it.Instead, such data will be collated after valid year numericdata for ascending order or before thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe year data for descending order.

are ignored, as for Y2C and Y2Z, except for data where the first byte beginswith X'00', X'40' or X'FF'.

an example, suppose you want to preserve the input order of header and trailer recordsat the start or end of the file, and your header/trailer records are identified by binaryzeros (X'00'), a blank (X'40') or binary ones (X'FF') in the first byte of the date field.

Y2S format allows CENTWIN to identify the header/trailer records and treat themdifferently from other records.Presuming the year data begins in column 20, you woulduse the following sort key specification:

.114 Programmer'sGuide

SORT SORT FIELDS=(20,2,Y2S,A)* Sorts yy field as 4-digit year

yy field (20,2) will be processed according to the century window setting. ForCENTWIN=1945, data with header and trailer records would be sorted as follows:

Input

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a'F9F6'

'4001'

'F4F4'

'4000'

'0000'

'F5F1'

'FF03'Record Order after SortingX'0000'X'4000'X'4001'X'F5F1'X'F9F6'X'F4F4'X'FF03'

that if the above data were sorted as Y2C or Y2Z format, the output order wouldbe different because the records starting with X'00', X'40' and X'FF' would be interpretedas numeric years.For example, suppose the fields in the above list were defined as Y2Zand sorted with EQUALS:

FIELDS=(20,2,Y2Z,A),EQUALS

data would be processed as follows:

Input

'F9F6'

'4001'

'F4F4'

'4000'

'0000'

'F5F1'

'FF03'Record Order after SortingX'F5F1'X'F9F6'X'FF03'(invalid numeric data)X'4000'(invalid numeric data)X'0000'(invalid numeric data)X'4001'(invalid numeric data)X'F4F4'

header and trailer records are sequenced as year data according to the CENTWINsetting (CENTWIN=19http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a45), and they lose their position at the start and end of the file.The PD0 Format

format is used to sequence 2-8 byte packed decimal data.PD0 ignores the first digitand trailing sign during processing.PD0 is normally used in conjunction with the Y2Pdata format.The Y2P format is used to process the 2-digit year portion of a packed dec-

2. SyncSort Control Statements2.115

SORT

date field, while the PD0 format is used to process the month and day portion of thefield.

PD0 is typically used with Y2P, the PD0 format itself is not affected byCENTWIN processing.

the packed decimal date field used in the example above:

= X'0yymmddC'

the trailing C (sometimes F) is a positive sign and the leading 0 pads the field onthe left to make an even number of digits.

that the components of the date span bytes:

y ym md dC://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adate can be processed as follows:

Y2P processes the year component X'0yym' as X'yy'.PD0 processes the month and day components X'ymmddC' as X'mmdd'.

following SORT control statement can be used to sort the entire date with CENTWINprocessing:SORT FIELDS=(20,2,Y2P,A, * Treats X'0yym' as X'yy'; sorts yy as yyyy

,3,PD0,A) * Treats X'ymmddC' as X'mmdd'

=COPY (Required for a Copy)

FIELDS=COPY to copy one or more input files.Multiple files can be copied if theyare concatenated to the SORTIN DD statement.Other control statements such asINCLUDE/OMIT, INREC, OUTREC and OUTFIL may be specified in conjunction witha copy application, allowing you to edit and reformat the file(s) without sorting them.The SUM control statement and an E32 exit cannot be specified with FIELDS=COPY.All Phase 3 exits can be used.

.116 Programmer'sGuide

SORT

/CHKPT Paramethttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aer (Optional)

CKPT/CHKPT parameter instructs SyncSort to take a checkpoint at every end-of-volume of a SORTOUT data set when OUTFIL is not used and also at the beginning ofPhase 3 before the SORTOUT data set is opened.Either spelling of this parameter isaccepted.

parameter requires a SORTCKPT DD statement.It cannot be specified in conjunc-tion with a user-issued STIMER macro or an incore sort.Checkpoints cannot be takenwithin a user exit routine.

to “Chapter 12. Performance Considerations” for an explanation of theCheckpoint/Restart feature.

Parameter (Optional)

format of the DYNALLOC parameter is illustrated below.       ,DYNALLOC            d  (nn,mm)     =  (d, n ,RETRY=     [,SC=s])

.DYNALLOC Parameter Format

requests the dynamic allocation of SORTWK data sets on device type d.Specify the device type either as a http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adecimal number (e.g., 3380) or by the system genericname (e.g., SYSDA).Any disk device accepted for a SORTWK DD statement can bespecified.Note that VIO is not accepted as a unit device.

that the DYNALLOC parameter may be used alone, without any subparameters.In this case, the DYNALLOC installation default settings are used.

MAXSORT applications, n is the number of SORTWK data sets that will be allocated.As many as 32 SORTWK data sets can be specified.The default for n is 3.

non-MAXSORT applications, n can be 1 through 100.This value specifies the numberof SORTWK data sets that can potentially be allocated.For values of n that are 31 orless, SyncSort can automatically raise the number to 32 if the application requires it.When n is 33 through 100, this value specifies the maximum number of SORTWK datasets that can be allocated.

=OFF can be specified to override a DYNALLOC=ON installatihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aon default.

2. SyncSort Control Statements2.117

SORT

for both MAXSORT and non-MAXSORT applications, any SORTWK data setsprovided in the JCL will contribute towards the value of n. For instance, if n was set to40 in a non-MAXSORT application and 30 SORTWKs were provided in the JCL,DYNALLOC could obtain 10 additional SORTWKs if needed. Note that there is an in-stallation option to disable DYNALLOC if SORTWKnn DD statements are present.

uses the value specified in the RETRY parameter to request automaticDYNALLOC retry. This facility attempts to avoid a sortwork capacity exceeded conditionwhen disk space is not immediately available to satisfy a DYNALLOC request. SyncSortwill automatically retry a specified number of times and wait a prescribed interval be-tween DYNALLOC requests.

nn in the first position designates the number of times SyncSort will retry a failedDYNALLhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOC request.The minimum allowed is 0 and the maximum is 16. The mm in thesecond position designates the number of minutes SyncSort waits between eachDYNALLOC request. The minimum allowed is 0 and the maximum is 15.A value of 0can be used to request an immediate retry.RETRY=OFF or an nn of 0 can be specifiedto override a RETRY=ON installation default.

an environment where DFSMS manages temporary work data sets, the SC subpa-rameter specifies a storage class s for SyncSort to use when dynamically allocatingSORTWORK data sets. The storage administrator at your installation defines the namesof the storage classes you can specify. Note that an installation written automatic classselection (ACS) routine can override the storage class you specify. If SMS is not installedor active to manage temporary work data sets, the d device specification will be used inthe SORTWORK dynalloc request.

/NOEQUALS Parameter (Optional)http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

EQUALS parameter insures that the original order of equal-keyed records is pre-served.These records will be in the same order in the output file as they were in theinput file.NOEQUALS, the default, specifies that equal-keyed records may not be writ-ten in their original input order.

the EQUALS parameter is used with the SUM control statement, the first of theequal-keyed records is retained with the sum; all other records are deleted after thespecifed field(s) have been summed.

/NOEQUALS can also be specified as a PARM option on the EXEC statement.If this option is specified both on the SORT statement and as a PARM option, the SORTspecification takes precedence.

is usually improved when NOEQUALS is in effect.

.118 Programmer'sGuide

SORT

Parameter (Optional)

FILSZ parameter specifies the actual (FILSZ=n) or estimated (FILSZ=En) decimalnumhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aber of records to be sorted.This number should reflect any changes produced byINCLUDE/OMIT, E14 and/or E15, SKIPREC and STOPAFT processing.

FILSZ=n is specified, SyncSort will terminate unless exactly n records are processed.If FILSZ is specified for a Tape Sort, use only the En specification.This value shouldindicate the number of records in the input file without taking into account records addedor deleted by an E14 or E15 exit.

can also be specified as a PARM option on the EXEC statement.If this option isspecified both on the SORT statement and as a PARM option, the PARM specificationtakes precedence.

Parameter (Optional)

SIZE parameter specifies the actual (SIZE=n) or estimated (SIZE=En) decimalnumber of records read from the input file.Unlike the FILSZ parameter, this numbershould not reflect any changes produced by INCLUDE/OMIT or exit processing, butshould reflect SKIPREC and STOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPAFT processing.

the FILSZ parameter is not specified and SIZE=n is specified, SyncSort will terminateunless exactly n records are processed.If the FILSZ parameter is specified, the SIZEvalue is considered an estimate whether or not it is preceded by an E.

Parameter (Optional)

SKIPREC=n parameter instructs SyncSort to skip a decimal number of records beforethe input file is sorted or copied.The n records skipped are deleted from the input filebefore E15 and INCLUDE/OMIT processing, if specified, take place.

SKIPREC is specified as a PARM option as well as on the SORT statement, the PARMspecification takes precedence.

Parameter (Optional)

STOPAFT=n parameter specifies the number of records to be sorted or copied.Thesewill be the first n records after E15, INCLUDE/OMIT and SKIPREC processing, if spec-ified, have completed.

STOPAFT is specified as a PARMhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a option as well as on the SORT statement, the PARMspecification takes precedence.

cannot be specified for a Tape Sort.

2. SyncSort Control Statements2.119

SORT

SORT Control Statements SORTFIELDS=(2.3,2,BI,D,8,2.4,BI,A,25,10,CH,A,15,10,LS,D)

.Sample SORT Control Statement

sample SORT control statement indicates four control fields:

The first, or primary, field begins in bit 4 of byte 2, is 2 bytes long, is in binary format

is to be sorted in descending order.

second control field begins in byte 8, is 2 bytes 4 bits long, is a binary format andis to be sorted in ascending order.

third control field begins on byte 25, is 10 bytes long, is in character format andis to be sorted in ascending order.

fourth control field begins on byte 15, is 10 bytes long, is an EBCDIC numericfield with a leading separate sihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1agn and is to be sorted in descending order.

FIELDS=(20,5,A,5,10,D,30,5,A),FORMAT=CH,CKPT

.Sample SORT Control Statement

sample SORT control statement specifies the following:

There are three control fields.Because all three fields have the same data format (in

case, character), the FORMAT=CH subparameter is specified so that the CHvalue does not have to be specified for each of the fields.

first control field begins on byte 20, is 5 bytes long and is to be sorted in as-cending order.

second control field begins on byte 5, is 10 bytes long and is to be sorted in de-scending order.

third control field begins on byte 30, is 5 bytes long and is to be sorted in as-cending order.

will take a checkpoint.

.120 Programmer'sGuide

SUM

Control Statement

SUM control statement deletes records whttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aith equal control fields and optionally sum-marizes specified numeric fields on those records.Equal keyed records are processed pairby pair.If numeric fields are to be summarized, the data in the summary fields is added,the sum is placed in one of the records, and the other record is deleted.Provided arith-metic overflow does not occur, the SUM statement produces only one record per sort keyin the output data set.The records deleted by sum can optionally be written to a separatedata set.

SUM control statement cannot be used when FIELDS=COPY is specified on theSORT or MERGE control statement or for a Tape Sort.

Control Statement Format

format of the SUM control statement is illustrated below.SUM   FIELDS=(p1,l1,f1 [,p2,l2,f2 ] ...)   FIELDS=(p1,l1 [,p2,l2 ] ...),FORMAT=f  [ ,XSUM ] FIELDS=NONE

.SUM Control Statement Format

Parameter (Required)

FIELDS parameterhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a defines the numeric fields to be summed when the control fieldsof two or more records are equal.Specify FIELDS=NONE to reduce the sorted data toone record per sort key without summarizing any numeric fields.

field specified in the FIELDS parameter is identified by its position p, length l andformat f.

position value indicates the first byte of the field relative to the beginning

the input record after INREC and/or E15 processing, if specified, have com-

.The field must begin on a byte boundary.

length value indicates the length of the field.The length must be an in-

number of bytes.Refer to the chart below for the permissible lengths.

format value indicates the data format.Fields with BI, FI, FL, PD and

formats can be summarized.If all the summary fields have the same for-

, you can specify the format value once by using the FORMAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aT=f subpa-

.If both the individual f values and the FORMAT subparameter are

, the individual f values will be used.(Note that f values must be

for each compare field.)lf

2. SyncSort Control Statements2.121

SUM

LENGTH2, 4, or 8 bytes2, 4, or 8 bytes4, 8, or 16 bytes1 to 16 bytes1 to 18 bytes

.Permissible Lengths for SUM FieldsXSUM Parameter (Optional)

the XSUM parameter if you want records deleted by SUM processing to be writtento a data set defined by the SORTXSUM DD statement.These records will be written toSORTXSUM at the time of SUM processing.The records will not undergo OUTREC, E35,and OUTFIL processing because such processing occurs after SUM processing.

DCB BLKSIZE of the SORTIN data set will not be used to determine the BLKSIZEofhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the SORTXSUM data set. System determined blocksize will be used when enabled andappropriate. Unblocked output will be generated if system determined blocksize has beendisabled and an explicitly specified blocksize has not been provided in the JCL.

XSUM file will be sequenced in the same order as the SORTOUT file.

that XSUM may increase system requirements:

Adding XSUM to an existing sort application may result in an increase in the amount

SORTWORK space required.This occurs because XSUM delays all summing untilPhase 3.

XSUM to an existing MAXSORT application could cause the generation ofadditional intermediate output files (SORTOU00 or SORTOUnn).This occurs be-cause XSUM delays SUM processing until the final MAXSORT merge pass.

may require additional main memory.Specify a region size of 512K or more.

.122 Programmer'sGuide

SUM

Conshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aiderations for SUM

If NOEQUALS is in effect, the record which is retained is determined arbitrarily.If

is in effect, the record which is retained is the first record read.TheEQUALS parameter can be specified on the SORT or MERGE statement or as aPARM option.

sort or merge control field cannot be summarized.A portion of a control fieldcannot be included in a sum field.

fields may not overlap each other.

-sum fields remain unchanged and are retained from the record which containsthe sum.

arithmetic overflow occurs during the summing of two records, those records arenot summarized and neither record is deleted.The sum process continues, however,so that if a subsequent pair of records with equal control fields can be summarizedwithout causing overflow, they will be summarized.To avoid arithmetic overflow,use the INREC statement to insert zeros of the proper format immediatelhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay before thesum field.For example, for a PD field, use nZ to insert binary zeros.

that the first 4 bytes of variable length records are reserved for the RecordDescriptor Word, so the first byte of the data portion of the record is byte 5.

is incompatible with an incore sort.If you specify the SUM control statement,allocate SORTWKnn data sets in the JCL or use the DYNALLOC feature for dynamicSORTWK allocation.If no JCL SORTWKs are provided and DYNALLOC is disabledby default, SUM will cause DYNALLOC to be enabled.

FL fields are summarized, user-issued SPIE macros are not permitted and exitroutines must not produce exponent overflow or underflow.Because of the numericrounding performed by the hardware, the exact sum depends on the order in whichfields are summed.Thus, the sum may vary slightly for different executions.

default, the sign byte of a positive summarized ZD field will be conhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1averted toprintable format.If you want to disable this action, use the NZDPRINT PARM op-tion. Refer to “ZDPRINT” on page 5.32.

SUM Control Statements

following SUM statement eliminates equal-keyed records without summarizing nu-meric fields.The XSUM option causes the eliminated records to be written to a data setdefined on the SORTXSUM DD statement.

2. SyncSort Control Statements2.123

SUM  SUMFIELDS=NONE,XSUM

.Sample SUM Control Statement

with equal control fields will be eliminated from SORTOUT or SORTOFnn datasets so that only one record is retained.

following SUM statement summarizes two numeric fields on records with equal con-trol fields. SUMFIELDS=(20,4,32,4),FORMAT=PD

.Sample SUM Control Statement

the control fields are equal, this SUM statement summarizes the numeric data inthe fields beginning in bytehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as 20 and 32.Because both fields are in packed decimal format,the FORMAT=PD subparameter is used so that the PD value does not have to be specifiedfor each field.

examples illustrating the SUM control statement are provided in “Chap-ter 3.How to Use SyncSort's Data Utility Features”.

.124 Programmer'sGuide

Chapter 3.How to Use SyncSort's Data Utility

chapter assumes that you already know how to sort records and are ready to useSyncSort's Data Utility features for any or all of the following:

Selecting only those input records and data fields that are needed for an application.Eliminating duplicate records.Consolidating records into a single record that contains the sum of any numeric datafields.

output data printable and easy to read.

a multi-sectioned report complete with headers and trailers.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

several output files and reports with a single pass of the sort.

following examples show how you can accomplish these tasks with SyncSort. Eachexample is self-contained and provides coding instructions for both the required JCL andthe necessary control http://www.wendangwang.come them as starting points for your own applications.For details of control statement syntax see &quot;Chapter 2. SyncSort Control Statements.&quot;

3. How to Use SyncSort's Data Utility Features3.1

Sample Data Utility Applications

following chart lists applications that demonstrate SyncSort's features.Feature

Input Records

Relevant Fields from

Input Records

Records within a File

Output Records Print-

and Easy to ReadApplicationIncluding Relevant RecordsOmitting Irrelevant RecordsSelecting a Number of Fielhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ads from Longer RecordsEliminating Irrelevant Data Field(s)Selecting Fields from Variable-Length RecordsCombining Records and Summing Numeric Data FieldsEliminating Duplicate RecordsReordering the Positions of Record FieldsInserting Blanks and Repositioning Record Fields

Binary Zeros

Unprintable Data to Readable Form

Unprintable Data to Hexadecimal Format

and Editing Unprintable Data

a Data Field in Standard Format

from Variable to Fixed Length Format

Input Records on Multiple Output Lines

Output into Sections

a Title Page for a Report

a Page Header

a Section Header

a Header to Eliminate Duplication Information

a Section

a Report Trailer or Summary

a Page Trailer

Data at the End of ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Report

Data at the End of a Page

Data at the End of a Section

Maximum, Minimum and Average Data in

Trailers

a Count of Data Records

a Cumulative (Running) Count of Data Re-

Several Output Files with Different Infor-

Identical Output Files to Different DevicesPage3.33.53.73.83.93.113.123.143.163.183.203.223.233.253.263.273.293.313.333.343.353.373.383.393.413.423.453.473.483.513.53Dividing a Report into SectionsWriting Headers and Trailers fora ReportTotaling and Subtotaling DataObtaining Maximum, Minimumand Average DataCounting Data RecordsCreating Multiple Output Files

.2 Programmer'sGuide

Selecting Input Records

only certain records from an input file are needed for an application, SyncSort al-lows you to set up one or more logical conditions fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aor including only those records.Alter-natively, you may specify conditions for omitting records from an application.Eachcondition is based on a comparison between two record fields or between a record fieldand a constant. You may specify the constant as a positive or negative decimal, ahexadecimal or binary constant, or a character literal.Multiple conditions may be spec-ified, provided you connect them with ANDs and ORs.

specify the conditions for selecting records, use the INCLUDE/OMIT control state-ment.For complete syntax, and examples of bit level criteria in record selection, see“INCLUDE/OMIT Control Statement” on page 2.16

processing variable length records, by default all fields specified must be containedwithin the record. If an application is expected to reference fields not completely containedwithin the record, refer to “VLTESTI” on page 5.31.VLTESTI provides for processing ofrecords that do not cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1antain all fields.

Relevant Records

: A school board requires a list of all students performing below their grade levelon standardized exams.(The record layout is given in Figure65 and a sample record isgiven in Figure

[此处图片未下载成功]

66.)

.Input Record Layout

3. How to Use SyncSort's Data Utility Features3.3

[此处图片未下载成功]

Figure66.Sample Student Record

generate the list, the following is coded://SUBLEVJOB

//EXEC PGM=SYNCSORT

//SYSOUT DD SYSOUT=*

//*

//SORTIN DD DSN=WWBRSM.STUDENTS,DISP=SHR

//SORTOUTDDSYSOUT=*

//SORTWK01 DDUNIT=SYSDA,

// SPACE=(CYL,15)

//SYSIN DD*

=(29,2,LT,25,2,OR,27,2,LT,25,2),

=PD

FIELDS=(1,14,CH,A)Gives the JobnameIdentifies the ProgramAssignsSyncSortMessages to I/O DeviceDefinesInputDataSetDefines Output Data SetDefihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anes IntermediateStorageSelectsRecordsSortsRecords

.JCL and Required Control Statements

: In this application, two comparisons are necessary to identify the recordsneeded for the list: the Grade field (25,2) has to be compared to the student's ReadingScore field (27,2) and to the Mathematics Score field (29,2).All numeric fields on thestudent records are in packed-decimal (PD) format.

two-clause INCLUDE statement (see Figure67) guarantees the selection of theneeded records from the file. The first clause (29,2,LT,25,2) guarantees that records withMath Scores less than the Grade field are INCLUDED. The second clause (27,2,LT,25,2)guarantees that records with Reading Scores less than the Grade field are also IN-CLUDED. The OR connecting the two clauses guarantees that if either or both of thescores are less than the Grade field, the record is selected.Finally, since all the fieldsare in packhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed-decimal format (PD), FORMAT=PD is specified.

sample record shown above will be INCLUDED because the student's Math Score(047F) is lower than the Grade level (050F).

.4 Programmer'sGuide

Omitting Irrelevant Records

: Records that have an Invoice Status Code of F (fully paid) are to be omitted inpreparing a list of only those customers with outstanding payments. (The input recordlayout is given in Figure68 and a sample input record is given in Figure

[此处图片未下载成功]

69.)

.

[此处图片未下载成功]

Input Record Layout

.Sample Input Record

produce this list of customers selected from the masterfile, the following is coded.

3. How to Use SyncSort's Data Utility Features3.5

//OUTPAYJOB

//EXECPGM=SYNCSORT

//SYSOUTDDSYSOUT=*

//*

//SORTINDDDSN=NEWINV,DISP=SHR

//SORTOUTDDSYSOUT=*

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar//SORTWK01 DDUNIT=SYSDA,SPACE=(CYL,20)

//SYSIN DD *

=(80,1,CH,EQ,C'F')

=(1,29,CH,A)Gives the JobnameIdentifies the ProgramAssigns SyncSort Messages toI/O DeviceDefines Input Data SetDefines Output Data SetDefines Intermediate StorageOmitsRecordsSortsRecords

.JCL and Required Control Statements

: In this application, a simple comparison is necessary to identify thosemasterfile records that are not needed: the Invoice Status Code field (80,1,CH) has to becompared to the constant 'F'.

OMIT statement's condition, 80,1,CH,EQ,C'F', (see Figure70) guarantees that in-voice records, like the sample record shown above, with the Invoice Status Code 'F' areomitted from the sort.

Relevant Fields from the Input Records

records often contain some information that is not relevant to a specific application.For example, records in a perhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asonnel masterfile might, in addition to addresses, includesalaries and other confidential information that is not required for preparing a mailinglist.

's Data Utility features allow you to select only those record fields that containnecessary data and to eliminate those that do not.More important, SyncSort enables youto do this editing before the records are sorted. As a result, the sort has fewer bytes tohandle and processing is more efficient.

complete syntax of the INREC control statement, see “INREC Control Statement” onpage 2.30.

FIELDS=(p1,l1[,p2,l2,...,pn,ln])

.

,lBasic INREC Statement FormatSpecify the beginning position and length in bytes of the input record's relevant

. When specifying contiguous fields, or fields that directly follow one an-

, you can simply indicate the starting position of the first field together

the chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aombined length of the fields that are contiguous.

.6 Programmer'sGuide

Selecting a Number of Fields from Longer Records

: A school wants to rank the entire student body by grade point index. This ap-plication simply requires selecting the two relevant fields out of all the fields in the stu-dent records and, then, sorting on the Grade Point Index field. (The Input Record layoutis given in Figure

[此处图片未下载成功]

72.)

.Input Record Layout

include only the relevant fields and generate the ranked list of students, the followingis coded: //RANKJOB

//EXECPGM=SYNCSORT

//SYSOUTDDSYSOUT=*

//*

//SORTINDDDSN=TOT.STUDENTS,DISP=SHR

//SORTOUTDDSYSOUT=*

//SORTWK01 DDSPACE=(CYL,10),UNIT=SYSDA

//SYSIN DD *

FIELDS=(1,9,

,2)

=(10,2,PD,D)Gives the JobnameIdentifies the ProgramAssigns SyncSort Messahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1agesto I/O DeviceDefines Input Data SetDefines Output Data SetDefines Intermediate StorageSelects Record FieldsSortsRecords

.JCL and Required Control Statements

shows the input record after INREC processing.

3. How to Use SyncSort's Data Utility Features3.7

[此处图片未下载成功]

Figure74.Form of Post-INREC Record

: Specifying the two relevant data fields--the Social Security Number (1,9)and the Grade Point Index (74,2)--on the INREC statementprovides the sort with nec-essary data for the application and eliminates the fields that are not relevant to the ap-plication. INREC processing thus shortens each record to just a little under 14% of itsoriginal size.

Irrelevant Data Field(s)

:For an inventory list, the price code on the masterfile records is not necessary.(The masterfile record layout is given in Figure

[此处图片未下载成功]://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar

75.)

.INPUT Record Layout

eliminate the Price Code field and generate the inventory list, the following is coded.

.8 Programmer'sGuide

//INVENTRJOB

//EXECPGM=SYNCSORT

//SYSOUTDDSYSOUT=*

//*

//SORTINDDDSN=INV.WARHOUS,DISP=SHR

//SORTOUTDDSYSOUT=*

//SORTWK01 DDSPACE=(CYL,15),UNIT=SYSDA

//SYSIN DD *

FIELDS=(1,17,

,3)

=(1,5,CH,A)

.

.

.Gives the JobnameIdentifies the ProgramAssigns SyncSort Messagesto I/O DeviceDefines Input Data SetDefines Output Data SetDefines Intermediate StorageSelects Record FieldsSortsRecords

.JCL and Required Control Statements

[此处图片未下载成功]

77 shows the input record after INREC processing.

.Post-INREC Record Layout

: Specifying only those fields that are necessary eliminates those http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athat are notnecessary for the application. The Price Code field (18,1) has not been specified on theINREC statement; it will be deleted from the input records before the records are sortedby item number for the list.

Fields from Variable-Length Records

: For each volume in its collection, a library requires the catalog number and anyinformation concerning translations, other volumes in a series, additional copies on file,and so on. The catalog file consists of variable-length records, and except for the catalognumber, the required information is contained in the variable-length portion of each re-cord. (The record layout is given in Figure78.)

3. How to Use SyncSort's Data Utility Features3.9

[此处图片未下载成功]

Figure78.Sample Record Layout

include only the relevant fields on the input records and to generate this list, the fol-lowing is coded. //LISTCATJOB

/http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a/EXECPGM=SYNCSORT

//SYSOUTDDSYSOUT=*

//*

//SORTINDDDSN=LIB.CATALOG,DISP=SHR

//SORTOUTDDSYSOUT=*

//SORTWK01 DDSPACE=(CYL,10),UNIT=SYSDA

//SYSIN DD *

FIELDS=(1,14,

)

=(5,10,ZD,A)

.

.

.Gives the JobnameIdentifies the ProgramAssigns SyncSort Messagesto I/O DeviceDefines Input Data SetDefines Output Data SetDefines Intermediate StorageSelects Record FieldsSortsRecords

.JCL and Required Control Statements

shows the input record after INREC processing.

.10 Programmer'sGuide

[此处图片未下载成功]

Figure80.Form of Post-INREC Record

: When selecting fields on variable-length records, you must observe these tworestrictions: (1) The position of the RDW cannot be affected; and (2) at least one byte fromthe fixed-length portion of the record, in addition to the RDW, must be specifihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed. On theabove INREC statement, the first 14 bytes of each record-the 4-byte RDW and the fixed-length Catalog Number field-are retained unchanged. The next field-which contains moreinformation, as required-is indicated only by position (98) since it is of variable-length.This causes the entire variable-length portion of the record (beginning with byte 98) tobe included after the initial 14 bytes of the post INREC record. SyncSort automaticallyadjusts the RDW to reflect the new record length.

Records within a File

you may want to shorten a file by consolidating records that have some in-formation in common. For example, a company's invoice file may contain more than onerecord for any customer to whom multiple invoices have been issued. In some applicationsit might then be feasible to consolidate such records--that is, to combine records withidentical Customer Name and Address fields into a single rhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aecord containing the sum ofthat customer's charges and payments.

SUM control statement allows you to combine records in this way.For SUM controlstatement syntax, see “SUM Control Statement” on page 2.121.

Records and Summing Numeric Data Fields

: For an inventory list, a company requires a single record for each product, in-dicating its item number, warehouse code, and the total quantity in stock.(Figure81gives the sample record layout.)

3. How to Use SyncSort's Data Utility Features3.11

[此处图片未下载成功]

Figure81.Input Record Layout

combine those inventory records with identical item numbers and warehouse codesand to produce the required list, the following is coded. //INVENTJOB

//EXECPGM=SYNCSORT

//SYSOUTDDSYSOUT=*

//*

//SORTINDDDSN=WRHSE.INVENT,DISP=SHR

//SORTOUTDDSYSOUT=*

//SORTWK01 DDSPACE=(CYL,6),UNIT=SYSDAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

//SYSIN DD *

=(6,1,CH,A,1,5,ZD,A)

=(7,12,PD)Gives the JobnameIdentifies the ProgramAssigns SyncSort Messagesto I/O DeviceDefines Input Data SetDefines Output Data SetDefines Intermediate StorageSortsRecordsCombines Records and

Numeric Data

.JCL and Required Control Statements

: The list is generated by sorting on the Warehouse Code field (6,1,CH) andthe Item Number field (1,5,ZD). Records that have identical information in both thesefields are combined into a single record that contains the sum or total of those records'Quantity fields (7,12,PD). That is, the single record will show how many items with thesame number are in each warehouse.

Duplicate Records

: A mailing list is being prepared from an invoice file. To eliminate duplicateentries, any multiple invoice records for the same customer are combined into a shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ainglerecord. (Figure83 gives the sample record layout.)

.12 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

Figure83.Input Record Layout

combine multiple invoice records and generate the mailing list, the following is coded.//MAILLISTJOBGives the Jobname

//EXECPGM=SYNCSORTIdentifies the Program

//SYSOUT DD SYSOUT=*AssignsSyncSortMessages//*to I/O Device

//SORTIN DD DSN=INV.MAST,DISP=SHR DefinesInputDataSet

//SORTOUTDDSYSOUT=*Defines Output Data Set

//SORTWK01DDSPACE=(CYL,5),UNIT=SYSDA Defines Intermediate Storage//SYSIN DD*

FIELDS=(17,28)Selects Relevant Fields

=(1,23,CH,A)Sorts Records. Reference is to

INREC Record

=NONEEliminates Duplicate Records

.JCL and Required Control Statements

: To prepare the customer mailing list, the only information required from theinvoicehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a records is located in the Company Name field (17,23) and the Address field (40,5),which are selected by the INREC statement. Sorting these records in ascending order bycompany name generates an alphabetical list.Then, because the file contains a recordfor every transaction, the SUM statement is used to avoid duplicate listings of customerswho have had more than one transaction.Note that because none of the fields containsnumeric data to be summed, the FIELDS=NONE parameter is used.

Output Records Printable and Easy to Read

data is usually stored in a compact format, it can be difficult, if not impossible,to read when printed. For example, on a typical input record, there will be no blank space

3. How to Use SyncSort's Data Utility Features3.13

between fields, numeric data will sometimes be lost in leading and trailing zeros, andsome data will be in unprintable format.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aer processing, you will probably want to edit this data so that it is easy to read. Thisis bound to entail one or more of the following tasks:

reordering the position of record fieldsinserting blanks between fieldsinserting binary zerosconverting numeric data from unprintable to printable formatconverting data to printable hexadecimal formatusing masks or edit patterns to insert dollar signs, decimal points, slashes, and the

.

the data in a record field on multiple output lines

's OUTREC processing, specified either as a control statement or as a parameteron the OUTFIL statement, can perform these and other editing functions. The OUTRECcontrol statement is described below. Any number of the OUTREC statement's subpa-rameters may be specified and must be coded in the order in which the fields will appearin the reformatted record. (Note thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahat when specified as a parameter of OUTFIL,OUTRECis coded identically as for a control statement except that the keyword FIELDS is notused.)See “OUTREC Control Statement Format” on page 2.75 for the complete formatof the OUTREC statement.

the Positions of Record Fields

: A data center has decided to reorder the positions of the data fields in masterfilerecords after sorting them.(Figure85 gives the layout for the masterfile record.)

.14 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

Figure85.Input Record Layout

sort the records alphabetically by product name and reposition the data fields, thefollowing is coded:

//SORTPRODJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program//SYSOUT DD SYSOUT=*AssignsSyncSortMessages //*to I/O Device//SORTIN DD DSN=PROD.SALES,DISP=SHR DefinesInputDataSet //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01DDSPAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCE=(CYL,10),UNIT=SYSDADefines Intermediate Storage //SYSINDD* SORTFIELDS=(7,15,CH,A)SortsRecords

FIELDS=(22,3,Repositions Fields on

,15,OutputRecords 1,2, 25,4, 3,4)

.JCL and Required Control Statements

shows the output record after OUTREC processing.

3. How to Use SyncSort's Data Utility Features3.15

[此处图片未下载成功]

[此处图片未下载成功]

Figure87.Post-OUTREC Record Layout

: After the records are sorted alphabetically by company name (7,15,CH),OUTREC processing moves the Product Code field (22,3) to the first byte of the record,the Product Name field (7,15) to the fourth byte, the Region field (1,2) to the nineteenthbyte, the Month's Sales field (25,4) to the twenty-first byte, and the Sales to Data field(3,4) to the twenty-fifth byte.

Blanks and Repositioning Record Fields

: The central office of a commhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aercial bank requires that each branch present itsmasterfile at the end of every month in the format outlined in Figure88, Branch A,however, has formatted its masterfile records as outlined in Figure

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

89.

88.RequiredFormat

.16 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

Figure89.Input Record Layout

reformat its masterfile records to conform to central-office specifications, the followingis coded. Since the records do not require sorting, the SyncSort copy feature is used.

//FORMATJOB //EXECPGM=SYNCSORT //SYSOUTDDSYSOUT=* //*

//SORTINDDDSN=ACCT.MAST,DISP=SHR //SORTOUTDDSYSOUT=*//SYSIN DD * SORTFIELDS=COPY

=(1,4,

,10, 6X, 5,3, 1X, 18,17)

the Jobname

the ProgramAssigns SyncSort Messagesto I/O Device

Input Data SetDefines Outpuhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at Data SetCopiesRecords

Fields onOutputRecords

.JCL and Required Control Statements

shows the effect of OUTREC processing on the output record.

3. How to Use SyncSort's Data Utility Features3.17

[此处图片未下载成功]

Figure91.Post-OUTREC Record Layout

: After the records are copied, OUTREC specifies two types of reformatting:(1) repositioning data fields and (2) inserting blanks between fields. As shown inFigure91, two fields have been repositioned: the Account Type field now begins on thetwenty-first byte as opposed to the fifth byte, and the Account Number field begins on thefifth byte rather than on the eighth. Also, blanks have been inserted using the nX entryto specify the number (n)of blanks. Six blanks have been inserted after the AccountNumber field and a single blank after the Account Type field. Since the Balance field andInterest fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aield are contiguous, they are treated as a single field in this application.

Binary Zeros

: A manufacturing firm has decided to expand its product line. However, becausethe Item Number field on its inventory records is too small, the records must be refor-matted to allow for more columns for the new products. The Item Number is kept inpacked-decimal, PD, format, and the firm wants to add 4 bytes to the current 2 byte field.The new bytes are to precede the current two bytes. Figure92 gives the input recordlayout.

.18 Programmer'sGuide

[此处图片未下载成功]

Figure92.Input Record Layout

copy the records and insert the 4 bytes of binary zeros, the following is coded.

//SORTCP //

//SYSOUT  //*

//SORTIN  //SORTOUT // //

PGM=SYNCSORTDD SYSOUT=*DD DD

=INV.REC,DISP=SHR

=INV.REC.OUT,DISP=(NEW,KEEP),UNIT=SYSDA,SPACE=(TRK,5)http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,VOL=SER=000111

the Jobname

the ProgramAssignsSyncSort

to I/O DeviceDefinesInputDataSetDefines Output Data Set

//SYSINDD* SORT FIELDS=COPY

=(1,20, 4Z, 25:21,56)

Binary Zeros &amp;ReformatsRecords

.JCL and Required Control Statements

effect of OUTREC processing is shown in Figure94 below.

3. How to Use SyncSort's Data Utility Features3.19

[此处图片未下载成功]

[此处图片未下载成功]

Figure94.Post-OUTREC Record Layout

: The records are copied, and OUTREC processing adds 4 bytes of binary ze-ros (4Z) to the beginning of the Item Number field (21,2). To allow for the 4 additionalbytes, the original Item Number field and the fields following it are all copied after the4 inserted bytes of zeros.

Unprintable Data to Readable Form

: For http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aa file of invoice records sorted by company name, the Invoice Amount,Amount Paid, and Balance Due fields are to be converted from packed-decimal to print-able format. In addition, any leading zeros will be suppressed and both commas anddecimal points will be inserted.(Figure

[此处图片未下载成功]

95 gives the input record layout.)

.Input Record Layout

sort the records, convert the three fields of packed-decimal data, and insert the com-mas and decimal points, the following is coded.

.20 Programmer'sGuide

//INVOICEJOB //EXECPGM=SYNCSORT //SYSOUTDDSYSOUT=* //*

//SORTINDDDSN=NEWINV,DISP=SHR //SORTOUTDDSYSOUT=* //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDA

//SYSIN DD * SORTFIELDS=(1,23,CH,A)

FIELDS=(17:1,23,

:24,4,PD,M2,

:28,4,PD,M2, 96:32,4,PD,M2)

the Jobname

the ProgramAssigns SyncSort

to I/O DeviceDefihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anes Input Data SetDefines Output Data SetDefines IntermediateStorage

Record Fieldsand Converts Data

.JCL and Required Control Statements

effect of OUTREC processing on the input record is shown in Figure

[此处图片未下载成功]

[此处图片未下载成功]

97 below.

.Post-OUTREC Record Layout

: First the records are sorted alphabetically by company name (1,23,CH).Then, three fields--the Invoice Amount (24,4,PD), the Amount Paid (28,4,PD), and theBalance Due (32,4,PD)--are converted from packed-decimal (PD) into readable format andediting by a SyncSort editing mask (M2) that suppresses the printing of leadingzerosand inserts the appropriate commas and decimal points. The number-colon entries (c:)that precede each of the four fields assign a new starting position or, when printing, col-umn for each of the four fields. For example, the Companhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay Name field, which originallybegan in byte 1 for a length of 23 bytes, now begins in byte 17; the Invoice Amount field,which began in byte 24, begins in byte 52, and so on. Note that after the data is convertedand edited, the lengths of the packed-decimal fields increase from four bytes each to tenbytes and that the fields are each separated by twelve blanks.

3. How to Use SyncSort's Data Utility Features3.21

Converting Unprintable Data to Hexadecimal Format

: A bank has discovered that some errors were made in recording the AccountNumbers of some of its customers.Specifically, on the transaction records, some AccountNumber fields, which should contain only packed-decimal, PD, data, appear to containdata that is not valid packed-decimal.Figure

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

98 shows the input record layout.

.Sample Input Record Layout

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarIn order to find the invalid data, the following is coded.

//SORTHEXJOB //EXECPGM=SYNCSORT //SYSOUTDDSYSOUT=* //*

//SORTINDD DSN=TRANS.RECS,DISP=SHR  //SORTOUTDDSYSOUT=*//SYSIN DD * SORTFIELDS=COPY

=(1,30,

:31,12,HEX)

the Jobname

the ProgramAssigns SyncSort

to I/O DeviceDefinesInputDataSetDefines Output Data SetCopiesRecords

Output Recordsand Converts Data

.JCL and Required Control Statements

effect of OUTREC processing on the input record is shown in Figure100.

.22 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

Figure100.Sample Post-OUTREC Record Layout

: The records are copied, and OUTREC processing reformats the output re-cord to contain the Customer Name field (1,30) followed in column 36 by the AccountNumber field converted to hexadecimal format (3http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a1,12,HEX). Blanks are automaticallyinserted in the unspecified columns (31,5). Note that converting the Account Number datato printable hexadecimal expands the original 12-byte field to 24 bytes. The bank can nowread the Account Number field in hexadecimal format to determine which records containinvalid data.

and Editing Unprintable Data

: For an Outstanding Payments report, the packed-decimal Amount Due field ona company's invoice records is converted to printable format and edited with a floatingdollar sign, commas, and a decimal point. In addition, to make the output easy to read,ten blanks are inserted between the Company Name field and the Amount Due field.(Figure

[此处图片未下载成功]

101 gives the input record layout.)

.Input Record Layout

.23

3. How to Use SyncSort's Data Utility Features

To sort the records and accomplish the conversion http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aand editing, the following is coded.

//PAYMNTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=INVOICE,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(1,23,CH,A)SortsRecords

=(1,23,Converts and Edits Data

X,and Inserts Blanks

,4,PD,EDIT=($II,IIT.TT))

.JCL and Required Control Statements

[此处图片未下载成功]

103 shows the effect of OUTREC processing on the input record.

.Post-OUTREC Record Layout

: First the records are sorted alphabetically by Company Name (1,23,CH).Next, OUTREC processing inserts 10 blanks (10X) between the Company Name field(1,23) and the Balance Due field (24,4,PD). OUTREC processing also converts thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aispacked-decimal field to printable format and edits it with the user-provided patternspecified on the EDIT subparameter, EDIT=($II,IIT.TT). This pattern provides for afloating dollar sign as well as the appropriate comma and decimal point. The Is indicatethat leading zeros should not be printed and the Ts indicate that zeros in those positionsshould be printed. Note that this conversion and editing of the data cause the length ofthe Balance Due field to increase from its original length of four bytes to ten bytes.

.24 Programmer'sGuide

Putting a Data Field in Standard Format

: The date field on insurance-policy records is stored in zoned-decimal format butwithout slashes separating the month, day, and year. After the records are sorted, theseslashes will be inserted and the date will appear in the standard mm/dd/yy format. (Fig-ure

[此处图片未下载成功]

104 gives the input record layout.)

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarFigure104.Input Record Layout

sort the records and format the date field with the required slashes, the following iscoded.

//SORTDTJOB //EXECPGM=SYNCSORT //SYSOUTDDSYSOUT=* //*

//SORTINDDDSN=NEW.POLCY,DISP=SHR //SORTOUTDDSYSOUT=* //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDA//SYSIN DD * SORTFIELDS=(1,23,CH,A)

FIELDS=(1:1,23,

:24,6,ZD,M9, 45:30,8)

the Jobname

the ProgramAssigns SyncSort Messagesto I/O Device

Input Data SetDefines Output Data Set

Intermediate StorageSortsRecords

Data and RepositionsRecordFields

.JCL and Required Control Statements

effect of OUTREC processing is shown in Figure106.

3. How to Use SyncSort's Data Utility Features3.25

[此处图片未下载成功]

Figure106.Post-OUTREC Record Layout

: The records are sorted alphabetically by Member http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aName (1,23,CH). TheOUTREC statement repositions the Effective Date field (24,6,ZD) and the Policy Numberfield (30,8,ZD) in columns 30 and 45 respectively, leaving blanks between each of thethree fields. In addition, the OUTREC statement edits the Effective Date field with anM9 editing mask that places slashes between the month, date, and year. Note that editingthe Date field increases its size from six to eight bytes.

from Variable to Fixed Length Format

:In this example, there are three output files.The first is variable and the re-maining two are fixed length format.The variable output file is the standard output filefrom the sort.In order to convert the output from variable to fixed length format, youshould specify CONVERT on the OUTREC parameters of each of your OUTFIL controlstatements.The following are the JCL and control statements to effect this result.

.26 Programmer'sGuide

http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a//JOB//EXECPGM=SYNCSORT//SYSOUTDDSYSOUT=*//SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDA//SORTINDDDSN=VARIN,DISP=SHR//SORTOUTDDUNIT=SYSDA,SPACE=(CYL,(1,1)),//DISP=(,PASS),DSN=&amp;&amp;VAROUT//SORTOF1DDUNIT=SYSDA,SPACE=(CYL,(1,1)),//DISP=(,PASS),DSN=&amp;&amp;FIX1OUT//SORTOF2DDUNIT=SYSDA,SPACE=(CYL,(1,1)),//DISP=(,PASS),DSN=&amp;&amp;FIX2OUT//SYSINDD*

=(1,23,CH,A,28,2,CH,A)OUTFILFILES=1,

=(28,2,CH,EQ,C'92'),OUTREC=(1,23),CONVERTOUTFILFILES=2,

=(28,2,CH,EQ,C'93'),OUTREC=(1,23),CONVERT

://www.wendangwang.coming the CONVERT Parameter

Input Records on Multiple Output Lines

:In this example, five input record fields, shown in Figure108, are copied to

[此处图片未下载成功]

an output file with each field printed as a separate output line.

.Input Record Layout

output lines are created by specifying a newline character, i.e. / (http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aslash), in theOUTREC parameter of an OUTFIL control statement. As shown in Figure109, thenewline character follows the specification of each input field's starting position andlength.

3. How to Use SyncSort's Data Utility Features3.27

//MULTILIN JOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=&amp;&amp;DATA,DISP=SHRDefines Input Data //*Set //SORTWK01 DDUNIT=SYSDA,SPACE=(CYL,(3,3)) Defines Intermediate //*Storage //SORTWK02 DDUNIT=SYSDA,SPACE=(CYL,(3,3)) Defines Intermediate //*Storage //SORTOUTDDSYSOUT=*Defines Output Data //*Set//SYSIN DD * SORTFIELDS=(101,40,CH,A)SortsRecords OUTFILCONVERT,ConvertsData

=('CUSTOMER ADDRESS LIST',3/), Prints a Page

* Header

=(101,40,/,Prints the Data in the

*Field and Starts a*New Output Line 141,25,/,AsAbove 166,25,/,AsAbove 191,30,/,AsAbove://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

,35,2/)As Above but Starts

*2 New Output Lines

.JCL and Control Statements for Multiline Output

SyncSort has printed the data in the COMPANY NAME field, it starts a new outputline, prints on it the data in the next field, CUSTOMER NAME, starts a new line, andso forth. After printing the contents of the last field (CITY, STATE AND ZIP), SyncSortcreates two new lines (2/).

provides an excerpt from the output file where the input record is formattedon multiple lines. A blank line appears in the second and third set of multi-line outputbecause the corresponding input record fields (i.e. CUSTOMER TITLE and CUSTOMERNAME) were blank.

.28 Programmer'sGuide

CUSTOMER ADDRESS LIST

'S ROD INC.DAVID LAURENCESYS PROG

YOUNGMAN BLVD.GREAT NECK

Set of Multiline Output

.06854

'S VISION TECHNOLOGYMR. N. FRYE261 ALBION http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPLACESEA BRIGHT

Set of Multiline Output

.08572

&amp; COMPANYDATA CENTER MANAGER300 DORIAN AVENUENEW YORK

Set of Multiline Output

.11220

.Sample Multiline Output

a Report into Sections

printing sorted output, you may want to divide it into sections. For example, aftersorting a personnel file alphabetically by company name and department, you might wantto print each department's records as a separate section and leave some blank lines be-tween each section. You might even want to print each section as a separate page of thereport. SyncSort allows you to print groups of records that have identical information inone or more sort fields as sections and to separate each section by a specified number oflines or a page break.

divide output into sections, use the SECTIONS parameter on the OUTFIL controlstatement.For complete syhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1antax of the SECTIONS parameter, see “SECTIONS Parame-ter (Optional)” on page 2.67.

Output into Sections

: A personnel roster is to be divided into sections by Department.(Figure111presents the layout for the input record.)

3. How to Use SyncSort's Data Utility Features3.29

[此处图片未下载成功]

[此处图片未下载成功]

Figure111.Input Record Layout

sort the records and generate a list that is divided by Department, the following iscoded.

//ROSTERJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=PRSNL,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,2),UNIT=SYSDADefines Intermediate Storage//SYSIN DD *

=(15,5,A,1,14,A),FORMAT=CH Sorts RecordsOUTFILOUTREC=(6:15,5,Repositions Record Fields

:1,14, 33:20,3, 44:23http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,1, 54:24,2), SECTIONS=(15,5,SKIP=5L)SectionsRecords

.JCL and Required Control Statements

sample of the listing generated is shown in Figure113.

.30 Programmer'sGuide

ACCTG  ACCTG ACCTG ACCTGACCTG  ACCTGACCTG BELL EMERYJONESNORTHOWEN TWAINWEST PATPAULMARKNANCYJERRY JOANDONNA SUPCLKCLKMGRCLKSECCLKFMMFMFF03040102030503

PRSNLPRSNL PRSNL PRSNLSMITHETOWERSVREES WUYOUNGJON LINDAGEORGE JANERUSSCLK CLKCLKSUPMGRMFMFM0002020503

113.SampleOutput

: After the records are sorted alphabetically by Department (15,5) and Em-ployee Name (1,14), they are divided into sections by department. That is, every timethere is a change in the Department field (15,5 in the input record) the printer skips 5lines (5L) before printing the next record. (Note, in the Sample Output above, the five-linebreak that occurs between ACCTG and PRSNL.) The OUTREC parameter is used to re-phttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aosition the record fields and to leave blanks between them.

Headers and Trailers for a Report

are used to provide report, page, and section headings such as titles, page num-bers, the current date, labels for each column of data, and the like. Similarly, trailers areused for report, page, and section summaries. You can use them, for example, to providetotals for columns of numeric data (see &quot;Totaling and Subtotaling Data&quot;) or to indicate theend of a section with, say, a string of asterisks or to provide a list of abbreviations usedin the report.

generate Headers and/or Trailers, use the HEADER and TRAILER parameters of theOUTFIL control statement.For complete syntax, see “HEADER1/HEADER2 Parameters(Optional)” on page 2.56 and “TRAILER Parameters (Optional)” on page 2.60

a Title Page for a Report

: Marketing wants a title page for its monthly departmentalhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a sales report. Thethree-line title will begin on line 16 and three blank lines will separate each line of thetitle. The three lines will start printing in columns 49, 59, and 63, respectively.To print this title page, the following is coded:

3. How to Use SyncSort's Data Utility Features3.31

//DSRPT//

//SYSOUT//*

//SORTIN//SORTOUT//SORTWK01//SYSIN  SORT

=SYNCSORTSYSOUT=*

=MRKTNG.SALES,DISP=SHRDDSYSOUT=*DD SPACE=(CYL,5),UNIT=SYSDA DD *

=(1,15,CH,A)SortsRecords...

=(15/,49:'D E P A R T M E N T A LS A L E S',

/,59:'F E B R U A R Y',4/,63:'1 9 9 2'),Generates Title Page

...

the Jobname

the ProgramAssigns SyncSort Messagesto I/O Device

Input Data SetDefines Output Data Set

.JCL and Required Control Stathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aements

shows the header that is generated by the above HEADER1 parameter:

E P A R T M E N T A L

E B R U A R Y

9 9 2

A L E S

115.SampleHEADER1

: The HEADER1parameter produces a header that will print on a separatepage, with no page number, at the beginning of the report.The first number-slash (n/)entry, 15/, causes the printer to skip 15 lines before printing. The following number-colonentry (c:), 49:, specifies the column in which the literal string 'D E P A R T M E N T ALS A L E S' begins to print. Note that the literal string prints exactly as it is enteredbetween the single quotes, with a space between each letter and a double space betweenthe words.

next entry, 4/, causes the printer to skip 3 more blank lines before starting to printthe literal string 'F E B R U A R Y' in column 59.

, three more lines are left blank (4http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a/) and the literal string '1 9 9 2' begins printingin column 63.

.32 Programmer'sGuide

Writing a Page Header

: Marketing wants the first line of every page of its departmental sales report tocontain the program number, report title, page number, and date. They want the thirdline of every page to contain an identifying label for each column of data. Each of theselines will begin printing in column one.

print the page header, the following is coded.

//DSRPTJOBGives the Jobname//EXECPGM=SYNCSORTIdentifies the Program//SYSOUTDDSYSOUT=*Assigns SyncSort Messages//*to I/O Device//SORTINDDDSN=MRKTNG.SALES,DISP=SHRDefines Input Data Set//SORTOUTDDSYSOUT=*Defines Output Data Set//SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(1,15,CH,A)SortsRecords . . . OUTFIL. .

=(1:'PGM NUMBER 5',

:'DEPARTMENT SALES REPORT FOR FEBRUARY 1992',://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar

:'DATE:',

:&amp;DATE,Generates Page Heading

:'PAGE:', 127:&amp;PAGE,//, 1:'DEPARTMENT', 40:'SALESMANAGER', 61:'SALESREP',

:'SALES THIS PERIOD',

:'SALES YEAR TO DATE',//),

. .

.JCL and Required Control Statements

shows a representation of the header that is generated by the aboveHEADER2 parameter.

NUMBER 5DEPARTMENT

SALES REPORT FOR FEBRUARY 1992

MANAGER

REP

THIS PERIOD

: 02/01/92

: 1

YEAR TO DATE

117.SampleHEADER2

3. How to Use SyncSort's Data Utility Features3.33

Explanation: The HEADER2 parameter produces the page header shown above. Becauseno forward spacing is specified, the page header begins on the first line of every page.Each of the HEADER2's number-colon entries (c:), for example, 1:, indicates the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acolumnin which the entry following the colon begins to print. Thus, the literal 'PGM NUMBER5' is printed beginning in column 1, and so on. The &amp;DATE and the &amp;PAGE entriesgenerate a current date and a consecutive page number, respectively. The date and thepage number appear after the labels DATE: and PAGE:, which are specified like the otherliterals.

double slashes (//) following the &amp;PAGE entry direct the printer to forward space twolines, that is, to leave one blank line, before printing the next group of literals that con-stitute the labels for the columns of data.

a Section Header

: Marketing wants each section of its departmental sales report to have its ownheading.The heading will consist of one line containing an identifying label for eachcolumn of data. The heading will begin printing in column one.To print the section header, the following is coded.

//DSRPTJOBGives http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe Jobname//EXECPGM=SYNCSORTIdentifies the Program//SYSOUTDDSYSOUT=*Assigns SyncSort Messages//*to I/O Device//SORTINDDDSN=MRKTNG.SALES,DISP=SHRDefines Input Data Set//SORTOUTDDSYSOUT=*Defines Output Data Set//SORTWK01DD SPACE=(CYL,5),UNIT=SYSDA DefinesIntermediateStorage//SYSIN DD * SORTFIELDS=(1,15,CH,A)SortsRecords

=(1:1,15,Repositions Fields on Output

:23,7,Records and Edits Data

:48,3, 72:60,4,PD,EDIT=($II,IIT.TT), 101:64,4,PD,EDIT=($II,IIT.TT), 114:C''), SECTIONS=(1,15,SKIP=5L, GeneratesSectionBreaks

=(1:'DEPARTMENT',Generates Section Headings

:'SALESMGR', 48:'SALESREP',

:'SALES THIS PERIOD',

:'SALES YEAR TO DATE',//))

.JCL and Required Control Statements

shows the header that is generated by the above HEADER3 subparameter.

.34 Programmer'sGuide

DEPARTMENTOVER COUNTEROVERCOUNTEROVERCOUNTEROVERCOUNTEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aROVERCOUNTER

MGRCASEYCASEY CASEY CASEY CASEY

REP075093 084 090 095

THIS PERIOD$14,000.0013,550.0011,755.0012,250.0013,075.00

YEAR TO DATE$27,000.0032,000.0024,850.0025,000.0026,180.00

SURGICAL SURGICAL SURGICAL  . . .

MGR.KILDARE KILDARE KILDARE KILDARE

...

REP003007009004...

THIS PERIOD$11,750.00$14,300.0011,110.0013,375.00

...

YEAR TO DATE$25,320.0024,900.0030,850.0027,505.00

...

.Sample Sections with HEADER3

: The HEADER3 subparameter on the SECTIONS parameter generates aheader that prints at the beginning of each section. Its primary purpose here is to providelabels for the columns of data that appear in each section. Each of the number-colon en-tries (c:) specifies the column in which the entry following it should begin to print. Thus,the literahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1al string 'DEPARTMENT' begins to print in column 1, the literal string 'SALESMGR' begins to print in column 23, and so on. Blanks are automatically inserted in thespace between the columns that are specified. On the OUTREC parameter a blank hasbeen inserted in column 114 (114:C' ') so that the output record length will equal that ofthe header. Note that if the HEADER3 in this example were used in conjunction with thepreceding HEADER2 example, there would be no need to specify the labels for the col-umns of data in the HEADER2.

a Header to Eliminate Duplicate Information within a Section

: Rather than repeat the department name and sales manager, which are iden-tical for every record included in a section of the departmental sales report, marketingwants this information to appear only once-within the section headers of the report.Therefore, the section headers' first two entries (Department and Sales Managehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar) will bedrawn directly from the first data record in each section.

print the section header with the input data fields, the following is coded.

3. How to Use SyncSort's Data Utility Features3.35

//DSRPTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=MRKTNG.SALES,DISP=SHR Defines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage //SYSIN DD * SORTFIELDS=(1,15,CH,A)SortsRecords . . .

...,Repositions Fields on Output

=(25:48,3,Records and Edits Data

:60,4,PD,EDIT=($II,IIT.TT), 56:64,4,PD,EDIT=($II,IIT.TT), 75:C''),

=(1,15,SKIP=2L,Generates Section BreaksHEADER3=(1:1,15,Generates Section Headings

:23,7, 22:'SALESREP',

:'SALES THIS PERIOD',54:'SALES YEAR TO DATE'))

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aure120.JCL and Required Control Statements

shows the header that is generated by the above HEADER3 subparameter.

COUNTER

REP

093 084 090 095

THIS PERIOD

$14,000.00 $13,550.00 $11,755.00 $12,250.00 $13,075.00

YEAR TO DATE$27,000.00$32,000.00$24,850.00$25,000.00$26,180.00

REP003 007 009 004 ...SALES THIS PERIOD$11,750.00 $14,300.00 $11,110.00 $13,375.00

...SALES YEAR TO DATE$25,320.00$24,900.00$30,850.00$27,505.00

...

.Sample Sections with HEADER3 Including Data from Input Record

.36 Programmer'sGuide

Explanation: The HEADER3 subparameter on the SECTIONS parameter generates aheader that prints at the beginning of each section. Its primary purpose here is to provideindividualized section headings that contain the Department Name and the Sales Man-http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aager from the records in that section as well as labels for the columns of data. The firsttwo entries in this header, 1:1.15 and 23:23,7 (the Department Name and Sales Manager,respectively), are drawn directly from the input record to eliminate the repetition of thesefields in the detail lines of each section. Note that specifying these fields in the HEADER3eliminates the need to include them in OUTREC processing as was necessary in thepreceding example. Each of the number-colon entries (c:) specifies the column in whichthe entry following it should begin to print. Thus, the Department field, (1,15) begins toprint in column 1; the Sales Manager field, in column 23; the literal string &quot;SALES REP&quot;,in column 48, and so on. Blanks are automatically inserted in the space between the col-umns that are specified. It should be pointed out that on the OUTREC parameter a blankhas been inserted in column 114 (114:C' ') so that the ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1autput record length will equal thatof the header.

a Report Trailer or Summary

: The final page of marketing's departmental sales report will contain a notesaying that February sales figures include residual 1992 sales not previously recorded.This note will begin on the 21st line of the page and start printing in the 33rd column ofthe page.

print the report trailer, the following is coded.

//DSRPTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=MRKTNG.SALES,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set  //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(1,15,CH,A)SortsRecords . . . OUTFIL. . .

Report TrailerTRAILER1=(20/,

:'FEBRUARY SALES FIGURES INCLUDE RESIDUAL 1992',

'SALES NOT PREVIOUSLY RECORDED')://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apar.JCL and Required Control Statements

shows the trailer that is generated by the above TRAILER1 parameter.

3. How to Use SyncSort's Data Utility Features3.37

FEBRUARY SALES FIGURES INCLUDE RESIDUAL 1992 SALES NOT PREVIOUSLY RECORDED

123.SampleTRAILER1

: The TRAILER1 parameter produces a report trailer or summary that con-stitutes the final page of a report. Unless otherwise specified, it begins on the first lineof the page. The TRAILER1's initial number-slash (n/) entry, 20/, directs the printer toforward space 20 blank lines before printing on the 21st line. The next entry, a number-colon (c:) entry, is used to center the literal string that follows it by having the string ofcharacters begin printing in the appropriate column. It specifies column 33 as the begin-ning position for printing the literal string, 'FEBRUARY SALES FIGURES INCLUDERESIDhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aUAL 1992 SALES NOT PREVIOUSLY RECORDED'.

a Page Trailer

: Marketing wants the last line on every page of its departmental-sales report tocontain a note identifying the information as confidential. This line will begin printing incolumn one.

print the page trailer, the following is coded.

//DSRPTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=MRKTNG.SALES,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(1,15,CH,A)SortsRecords . . . OUTFIL. . .

=(5'*','C O N F I D E N T I A LI N F O R M A T I O N',5'*','C O N F I D E N T I A LI N F O R M A T I O N',5'*')

.

.Generates Page Trailer

.

.JCL and Required Control Statements

shhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aows the trailer that is generated by the above TRAILER2 parameter.

.38 Programmer'sGuide

*****CONFIDENTIAL INFORMATION*****CONFIDENTIAL INFORMATION*****

125.SampleTRAILER3

: The TRAILER2 coded above provides a trailer that appears at the bottomof every logical page. The first entry, 5'*', a literal enclosed in single quotes (in this casean asterisk) and a repetition factor (5), specifies that 5 asterisks should be printed. Be-cause no column was specified, the trailer begins in column one. The next entry, 'C O NF I D E N T I A LI N F O R M A T I O N ', specifies that the literal string enclosed inthe single quotes should directly follow the asterisks. Note that the literal string isprinted exactly as it is coded within the quotation marks. That is, there is a blank be-tween every letter and two blanks between each word.The trailer's other entries specifythe printing of another five ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asterisks followed by the literal string 'C O N F I D E N T IA LI N F O R M A T I O N ' and finally another five asterisks.

and Subtotaling Data

a summary or trailer for a report will sometimes involve providing totals for col-umns of figures.For example, you would probably want a trailer for an inventory reportto contain the total number of items on hand. The OUTFIL statement allows you to writetrailers that contain both totals and subtotals. Moreover, you can total data at the endof a report, at the end of a page, and also at the end of a section.

generated total and subtotals, use the TOTAL and SUBTOTAL entries of OUTFIL'sTRAILER parameters and subparameter.For details of syntax, see “TRAILER Parame-ters (Optional)” on page 2.60

Data at the End of a Report

: The departmental sales report's final page will be a summary containing boththe total for the sales thihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as period and the total for the sales to date.The trailer will beginon the 21st line of the page and each total will have an identifying label.To print the report trailer, the following is coded.

3. How to Use SyncSort's Data Utility Features3.39

//DSRPTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device  //SORTINDDDSN=MRKTNG.SALES,Defines Input Data Set DISP=SHR //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),Defines Intermediate Storage UNIT=SYSDA//SYSIN DD *

FIELDS=(1,15,CH,A)Sorts Records  . . . OUTFIL. . .

Report Trailer with TotalsTRAILER1=(20/,

:'SALES THIS PERIOD:',

:TOT=(24,4,PD,EDIT=($II,IIT.TT)),

:'SALES TO DATE:',

:TOT=(28,4,PD,EDIT=($II,IIT.TT)))

.JCL and Required Control Statements

shows the trailer that is http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1agenerated by the above TRAILER1 parameter.

THIS PERIOD: $35,807.85

TO DATE: $62,305.25

127.SampleTRAILER1

: The TRAILER1 parameter produces a report trailer or summary that con-stitutes the final page of a report.Unless otherwise specified, it begins on the first lineof the page. This TRAILER1's initial number-slash(n/) entry, 20/, directs the printer toforward space 20 blank lines before printing. The next entry, a number-colon (c:) entry,is used to center the literal string that follows it by having the string of characters beginprinting in the appropriate column. It specifies column 40 as the beginning position forthe literal string 'SALES THIS PERIOD:' that labels the numeric data following it. ThisTRAILER's other number-colon plus literal-string entry functions the same way.The two TOT entries, TOT=(....), generate the trailer's totals. These entries specify thenumeric http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adata used and its format. Thus the four bytes of packed-decimal data that beginin byte 24 (24,4,PD) and the four bytes that begin in byte 28 (28,4,PD) of the input recordare converted to printable format. This data is then edited by the EDIT pattern($II,IIT.TT), which suppresses the printing of leading zeros and inserts a floating dollarsign as well as a necessary comma and decimal point. The pattern uses an I to indicatethose zeros in the total that should not be printed and a T to indicate those that should.Note:Be sure to code all the necessary parentheses when using the TOTAL and EDITentries.

.40 Programmer'sGuide

Subtotaling Data at the End of a Page

: The page trailer for a report listing invoices is to contain the totals for theAmount Paid and the Balance Due fields of the invoice records printed up to and includingthat page. These totals will appear directly below the columns of figures and behttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a separatedfrom them by strings of hyphens. An identifying label, TOTALS:, will appear on the sameline as the totals and will begin in column 40.To generate the trailer, the following is coded.

//INVLSTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program  //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=INVOICE,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDA Defines Intermediate Storage//SYSIN DD *

=(9,23,A,36,2,A,32,4,A), Sorts Records

=CH . . . OUTFIL. . .

=(65:10'-', 86:10'-',/, Generates Page Trailer

:'TOTALS:',with Running Totals

:SUB=(46,4,PD,EDIT=($II,IIT.TT)), 86:SUB=(54,4,PD,EDIT=($II,IIT.TT)))

.JCL and Required Control Statements

shows the trailer that is produced.

3. How to Use SyncSort's Data Utility Featurehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as3.41

. . .

TRUST COMEWER COLLEGENORTHEAST INDUSTPARK PLACE CORPPATIO PRODUCTSPINES ASSOCIATESPOLL DATA CORPPRIESTLEY METALSREGENCY TRUST COREPUBLIC DATA

RICE FEATURESRICE FEATURESRICE FEATURESROBINS NEST CORPSIDNEY COLLEGESIDNEY COLLEGE

...

821240158301329883022198830133538212401683013297...

/15/921/17/921/17/922/15/922/15/922/15/9212/15/922/15/9212/15/921/17/9212/15/9212/15/921/17/922/15/921/17/9212/15/921/17/92TOTALS: ...0.000.00200.000.000.000.000.000.000.000.000.00750.000.000.000.000.000.00-------$6,150.00 ...1,500.001,500.00200.00650.00850.00750.00600.001,600.001,500.001,100.00360.00750.001,500.001,500.00900.005,000.002,500.00----------$66,475.00

.TRAILER2 with SUBTOTAL

: The above TRAILER2 provides for totaling the figures in the Amhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aount Paidfield (46,4,PD) and the Amount Due field (54,4,PD) on the invoice records. Because theSUB (SUBTOTAL) entry is specified, the totals that appear at the bottom of each pagerepresent running totals, that is, the totals for all the records that have been printed upto and including that page. The TRAILER2 also generates the identifying label TOTALS:(40:'TOTALS:') and strings of hyphens at the bottoms of the columns to be totaled (65:10'-',86:10'-').

totaled data for each field is converted to printable format and, after being edited,begins printing in the columns specified with the two number colon entries (c:), 65: and86:. The data is edited by the EDIT pattern, ($II,IIT.TT), which suppresses the printingof leading zeros and inserts a floating dollar sign as well as the necessary comma anddecimal point. The pattern uses an I to indicate the zeros in the total that should not beprinted and a T to indicate those that http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ashould.

Data at the End of a Section

: The section trailer for an accounts receivable report sectioned by month is tocontain the totals for the Amount Paid and the Balance Due columns of each section.These totals will appear directly below the columns of figures and be separated from themby strings of hyphens. An identifying label, TOTALS:, will appear on the same line as thetotals and will begin in column 40.

generate the trailer, the following is coded.

.42 Programmer'sGuide

//ACTRECJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=NEW.INV,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(9,23,A,36,2,A,32,4,A),SortsRecords FORMAT=CH . . . OUTFIL. . .

=(32,4,SKIPhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a=3L,Generates Section BreaksTRAILER3=(65:10'-',86:10'-',/,Generates Section Trailer

:'TOTALS:',withTotals 65:TOT=(46,4,PD,EDIT=($II,IIT.TT)), 86:TOT=(54,4,PD,EDIT=($II,IIT.TT))))

.JCL and Required Control Statements

shows the section trailer, with totals, that is produced.

3. How to Use SyncSort's Data Utility Features3.43

. . .

INDUST

...

TOTALS:

...

/15/91

...

.00---------$2,600.000.000.000.000.000.000.002,000.00

.000.002,000.00

.000.00200.000.000.000.000.00200.000.000.000.00----------$4,400.00

...

.00----------$19,770.007,500.001,100.00950.00850.00550.00550.003,000.00600.002,500.003,000.001,500.001,500.00200.001,100.001,500.00900.002,500.00200.00650.001,500.00650.00---------$32,800.00

FRAGRANCES83013304CHARACTER DATA83013343COUNTRY INDUSTRIAL830135http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a57DUNHAM INDUST INC83013302ECHO LABS INC83013300ESS SECURITIES83013311EVERMOREINDUST83013556 GOODEY FOODS83013356GROSS BOOKS CO83013264HARVEY MOTORS CO83013301KALABRACORPORATION 83013555 MEWER COLLEGE83013324NORTHEAST INDUST83013303REPUBLIC DATA83013306RICE FEATURES83013298ROBINS NEST CORP83013353SIDNEY COLLEGE83013297SOUTHWEST INDUST83013503SPENSERS INDUST83013989UNITED INTERESTS INC83013309WINIFRED INDUST83013299  TOTALS:

/17/92

/17/921/17/921/17/921/17/921/17/921/17/92 1/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/92

.TRAILER3 with TOTAL

: In addition to generating strings of hyphens at the bottom of the columnsto be totaled (65:10'-',86:10'-') and the identifying label TOTALS: on the line below(40:'TOTALS:'), the TRAILER3 provides for totaling the figures in the Amount Paid field(46,4,PD) and the Amount Due field (54,4,PD) on thehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a invoice records. Note that becausethe TOT (TOTAL) entry is specified, the totals that appear at the end of each sectionrepresent that totals only for the records that are included in that section.

totaled data for each field is converted to printable format and, after being edited,begins printing in the columns specified with the two number colon entries (c:), 65: and86:. The data is edited by the EDIT pattern, ($II,IIT.TT), which suppresses the printingof leading zeros and inserts a floating dollar sign as well as the necessary comma anddecimal point. The pattern uses an I to indicate the zeros in the total that should not beprinted and a T to indicate those that should.

.44 Programmer'sGuide

Obtaining Maximum, Minimum and Average Data

report may need to include maximum, minimum, and average data.The parametersprovided for this type of reporting are MIN, SUBMIN, MAX, SUBMAX, AVG andSUBAVG.The http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asyntax is the same as for TOTAL and SUBTOTAL.See “Totaling andSubtotaling Data” on page 3.39 and “TRAILER Parameters (Optional)” on page 2.60.

Maximum, Minimum and Average Data in Section Trailers

: The section trailers for an accounts receivable report sectioned by data group(AAA, BBB, etc.)are to contain six edited numeric values for a 6-byte field that beginsat byte 8 (8,6).The values to be printed are the following:

miminum data value up to that point in the report (SUBMIN)The miminum data value in the section (MIN)

maximum data value up to that point in the report (SUBMAX)The maximum data value in the section (MAX)

average data value up to that point in the report (SUBAVG)The average data value in the section (AVG)

value will be preceded, on the same line, by appropriate identifying text.Two col-umns of data will be printed.

print the rehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aport, the following is coded:

FIELDS=(1,3,CH,A,5,2,CH,A)SORT DATA BY GROUP AND SECTION OUTFILFILES=(OUT), SECTIONS=(1,3,SKIP=3L,

=(3:'GROUP',2X,1,3,/,16:'SECTION',6X,'VALUE',/),

=(//,4:'MINIMUM VALUE TO THIS POINT= ',

:SUBMIN=(8,6,ZD,M2),/,

:'MINIMUM VALUE FOR THIS GROUP= ',

:MIN=(8,6,ZD,M2),//,

:'MAXIMUM VALUE TO THIS POINT= ',

:SUBMAX=(8,6,ZD,M2),/,

:'MAXIMUM VALUE FOR THIS GROUP= ',

:MAX=(8,6,ZD,M2),//,

:'AVERAGE VALUE TO THIS POINT= ',

:SUBAVG=(8,6,ZD,M2)/,

:'AVERAGE VALUE FOR THIS GROUP= ',

:AVG=(8,6,ZD,M2))), OUTREC=(18:5,2,26:8,6,ZD,M2,80:1X)

following shows two sections from the report, with the resulting values for submini-mums, minimums, submaximums, maximums, subaverages and averages:

3. How to Use SyncSort's Data Utility Features3.45

GROUP AAA

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCTION010101020202030303

.42923.128,756.339,723.63

.43175.66645.83673.4123.71

VALUE TO THIS POINT=MINIMUM VALUE FOR THIS GROUP=MAXIMUM VALUE TO THIS POINT=MAXIMUM VALUE FOR THIS GROUP=AVERAGE VALUE TO THIS POINT=AVERAGE VALUE FOR THIS GROUP=

.7123.719,723.639,723.632,336.392,336.39

BBB

.01456.11874.014,354.002,583.54

.57809.01934.53853.21

VALUE TO THIS POINT=MINIMUM VALUE FOR THIS GROUP=MAXIMUM VALUE TO THIS POINT=MAXIMUM VALUE FOR THIS GROUP=AVERAGE VALUE TO THIS POINT=AVERAGE VALUE FOR THIS GROUP=

.010.019,723.634,354.001,771.971,207.55

: The SECTION parameter generates a section break on field 1,3, whichidentifies data groups (AAA, BBB, etc.).The HEADER3 parameter defines sectionheaders that print the label &quot;GROUP&quot; followed by the data group identifier.HEADER3

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a3.46 Programmer'sGuide

also defines two column headings: &quot;SECTION,&quot; which identifies the column containingsection numbers, and &quot;VALUE,&quot; which identifies the columns containing the numericdata.

TRAILER3 subparameters are SUBMIN, MIN, SUBMAX, MAX, SUBAVG and AVG.They specify the six values to appear in the section trailer.The values are all derivedfrom the same field (8,6) and are suitably edited with mask M2 (8,6,ZD,M2).

OUTREC parameter places the two data fields (5,2 and 8,6) in the report and editsthe 8,6 field in the same way as for the six values in the section trailer (8,6,ZD,M2).Theblank space placed at position 80 (80:1X) ensures that the output record is long enoughto contain the header records.

Data Records

in a report will sometimes require you to obtain a record count or a count for aparticular type of item in a specific part of a report. http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aThe OUTFIL statement allows youto write trailers that contain such a count as well as cumulative, or running, counts ofrecords. Moreover, you can obtain these counts at the end of a report, at the end of a page,and at the end of a section.

generate these counts, use the COUNT and SUBCOUNT subparameters (or COUNT15and SUBCOUNT15).These subparameters can be used in conjunction with all otherTRAILER entries.For syntax of COUNT and SUBCOUNT (as well as COUNT15 andSUBCOUNT15), see “TRAILER Parameters (Optional)” on page 2.60.

a Count of Data Records

: Marketing wants a count of the total number of customers with outstandingpayments included in the summary of its outstanding invoices report.

get this record count and print it as part of the report summary, the following is coded.

3. How to Use SyncSort's Data Utility Features3.47

//INVLSTJOBGives the Jobname //EXEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=INVOICE,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage//SYSIN DD * SORTFIELDS=(1,23,CH,A)SortsRecords . . . OUTFIL. . .

=(20/,Generates Report Summary

:'NUMBER OF CUSTOMERS WITH OUTSTANDING PAYMENTS:',

)

.JCL and Required Control Statements

shows the trailer containing the record count.

OF CUSTOMERS WITH OUTSTANDING PAYMENTS:52

.Report Trailer Containing Record Count

: Since each record in the report represents an individual customer, codingthe COUNT entry in the TRAILER1 will provide the total number of customers withoutstanding payments. This TRAILER1 produces a report trailer, or summary, that con-stitutes the finhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aal page of a report.It will print on the 21st line of the page (20/) and beginprinting the literal string 'NUMBER OF CUSTOMERS WITH OUTSTANDING PAY-MENTS: ' in column 40.

a Cumulative (Running) Count of Data Records

: For an outstanding invoices report sectioned by month, marketing wants a cu-mulative, or running, count of invoices to date at the end of each section as well as a totalcount of each month's invoices included as section trailers.To generate these record counts, the following is coded.

.48 Programmer'sGuide

//INVLSTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program //SYSOUTDDSYSOUT=*Assigns SyncSort Messages //*to I/O Device //SORTINDDDSN=INVOICE,DISP=SHRDefines Input Data Set //SORTOUTDDSYSOUT=*Defines Output Data Set //SORTWK01 DDSPACE=(CYL,5),UNIT=SYSDADefines Intermediate Storage //SYSIN* SORTFIELDS=(28,2,ZD,A,SortsRecords 24,2,ZD,A, 1,23,ZD,A) . . . OUTFILhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a. . .

=(24,6,SKIP=1L,Generates Sections with RecordTRAILER3=(/,Count &amp; Cumulative Record Subcount

:'MONTH''S NUMBER OF INVOICES: ',COUNT,/,95:'NUMBER OF INVOICES TO DATE: ',SUBCOUNT))

.JCL and Required Control Statements

shows the trailers containing the counts of records.

3. How to Use SyncSort's Data Utility Features3.49

...

TECHNOLOGIESRICE FEATURESSIDNEY COLLEGESNAP FEATURESWEBB BROS CORP

IMPORTSWINIFRED INDUST. . . 2/15/9112/15/9112/15/9112/15/9112/15/9112/15/9112/15/91. . . 360.00750.005,000.00750.00600.00750.00350.00...21.6075.00300.0075.0036.0045.0026.00

'S NUMBER OF INVOICES: 17NUMBER OF INVOICES TO DATE: 17

FRAGRANCESCHARACTER DATA

INDUSTRIALDUNHAM INDUST COECHO LABS INCESS SECURITIESEVERMORE INDUSTGOODEY FOODSGROSS BOOKS COHARVEY MOTORS COKALABRA CORPMEWER COLLEGENOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aRTHEAST INDUSTREPUBLIC DATARICE FEATURESROBINS NEST CORPSIDNEY COLLEGESOUTHWEST INDUSTSPENSERS INDUSTUNITED INTERESTSWINIFRED INDUST1/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/921/17/927,500.001,100.00850.00850.00550.00550.003,000.00600.002,500.003,000.001,500.001,500.00200.001,100.001,500.00900.002,500.00200.00650.001,500.00650.00618.7550.750.000.0022.0022.00225.0030.00150.00225.0090.0075.0020.0090.7575.0054.00150.0020.0026.0090.0026.00

'S NUMBER OF INVOICES: 21NUMBER OF INVOICES TO DATE: 38

AVENUE CORPBATHO PRODUCTSCARRINGTON OILCDR TRUST INCECHO LABS INCESS SECURITIESFASTEROOT EQUIPFEDERAL FABRICS

...2/15/922/15/922/15/922/15/922/15/922/15/922/15/922/15/92. . . 650.00850.001,600.001,500.00550.00550.001,700.001,750.00

. . . 29.2551.0064.0075.0022.0022.0076.5070.00...

.TRAILER3 Contahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aining Record Counts and Cumulative Record Counts

: The trailer's first / entry causes the printer to leave one blank line after thedata records and before printing the trailer. The second / entry indicates the end of thetrailer's first line. The identical number-colon entries (95:) set thestarting positions of

.50 Programmer'sGuide

the literal strings that follow them: 'MONTH' 'S NUMBER OF INVOICES: ' and 'NUM-BER OF INVOICES TO DATE: '.(Note that the apostrophe in MONTH'S is doubled be-cause a single apostrophe would signal the end of a literal string.) Finally, because eachdata record in this report represents an invoice, the TRAILER3's COUNT entry generatesa count of each month's invoices and the SUBCOUNT entry generates a cumulative, orrunning, count of the invoices. The leading zeros in these 8-byte fields are suppressed.

Multiple Output Files

centers often use thehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a same masterfile for different purposes. Assume, for example,that you wanted to produce two reports using a masterfile of cash-receipt records. Onereport was to present the total cash receipts for the current month; the second, for theyear to date. This would typically entail running a separate sort for each report.SortWriter's multiple-output feature, however, enables you to produce both reports witha single pass of the sort. In addition, you can specify the same or different devices to re-ceive the separate output files.

:All the output files will be sequenced in the same way, as specified on the SORTor MERGE statement.If you need to sort the output files differently, you should usePipeSort, a Syncsort product that works with SyncSort MVS to reduce total elapsed timeby generating multiple, differently sequenced output files from a single read of the inputdata.

generate multiple output files, code the OUTFIL shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atatement.For syntax of the OUTFILcontrol statement, see “OUTFIL Control Statement” on page 2.48.

Several Output Files with Different Information

: Marketing wants three output files of customer records. The first will containa list of U.S. and European customers. The second will contain a list of U.S. customersonly, and the third will contain a list of European customers only.To generate the three separate files, the following is coded.

3. How to Use SyncSort's Data Utility Features3.51

//CUSTRCD //

//SYSOUT //*

//SORTIN // //

//SORTOF1 // //* //

//SORTOF2

=SYNCSORTSYSOUT=A

=SALES.RECORDS,VOL=SER=DISK1,DISP=SHR

=SORTED.CUSTM.RECORDS,UNIT=TAPE,VOL=SER=112231,

the Jobname

the ProgramAssigns SyncSort Messagesto I/O Device

Input Data Set

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aes First Output DataSet Containing AllCustomer Records

=(NEW,KEEP)

=SORTED.DCUSTM.RECORDS, Defines Second Output Data

Containing Domestic

//UNIT=TAPE,VOL=SER=112232,Customer Records Only //DISP=(NEW,KEEP) //SORTOF3DDDSN=SORTED.ECUSTM.RECORDS, Defines Third Output Data //*Set Containing European  //UNIT=TAPE,VOL=SER=112233,Customers Only //DISP=(NEW,KEEP) //SORTWK01 DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage //SORTWK02 DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage //SORTWK03 DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage//SYSIN DD *

SORTFIELDS=(10,15,CH,A)

=1,OUTFIL Statement for SORTOF1

=ALLIncluding All Records

=2,OUTFIL Statement for SORTOF2

=(67,3,CH,EQ,C'USA')Including USA Records

=3,OUTFIL Statement for SORTOF3

=(67,3,CH,EQ,C'EUR')Including http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aEur. Records

.JCL and Required Control Statements

: Creating the three requested output files requires coding three

statements in the JCL: SORTOF1, SORTOF2, and SORTOF3 as well asthree OUTFIL statements. Each of the OUTFIL statements is connected by a FILES pa-rameter to one of the output files defined in the JCL. Specifying 1 on the FILES param-eter connects its OUTFIL statement with the output file defined by the SORTOF1 DDstatement in the JCL. Likewise, specifying 2 connects its OUTFIL statement with theoutput file defined by SORTOF2, and so on. The first output file will contain all the re-cords from the input file (INCLUDE=ALL). The second output file will include only thoserecords that contain the character string 'USA' beginning in byte 67,(INCLUDE=(67,3,CH,EQ,C'USA') ), which indicates that these records are for USA cus-tomers. And similarly, the third output file will inclhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aude only those records that containthe character string 'EUR' beginning in byte 67, which indicates that these records arefor European customers.

.52 Programmer'sGuide

Writing Identical Output Files to Different Devices

: Personnel wants a printed copy of its updated masterfile as well as copies ondisk and on tape.

generate these three copies of the same file on different devices, the following is coded.

//MULTOUTJOBGives the Jobname //EXECPGM=SYNCSORTIdentifies the Program//SYSOUT DD SYSOUT=*AssignsSyncSortMessages //*to I/O Device//SORTIN DD DSN=PERSNL.RECORDS,DefinesInputDataSet //VOL=SER=DISK1, //DISP=SHR //SORTOFPRDDSYSOUT=*Defines Printed Output //*Data Set //SORTOFTPDDDSN=PERSNL.RECORDS.TAPE,Defines Tape Output Data Set //UNIT=TAPE,VOL=SER=112233, //DISP=(NEW,KEEP) //SORTOFDSDDDSN=PERSNL.RECORDS.DISK,Defines Disk Output Data Set //UNIT=DISK1,DISP=(NEW,KEEP), //SPACE=(CYL,60) //http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSORTWK01DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage //SORTWK02DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage //SORTWK03DDSPACE=(CYL,20),UNIT=SYSDADefines Intermediate Storage //SYSINDD* SORTFIELDS=(1,40,CH,A)SortsRecords

FILES=(PR,TP,DS)Creates Multiple Output

.JCL and Required Control Statements

: Creating the three copies of the updated masterfile requires coding only one

statement with a FILES parameter. The FILES parameter instructs SyncSortto look for multiple output files defined in the JCL and to send its output to the devicesspecified in the SORTOFxx statements. Thus, the output that has been sorted as specifiedon the SORT statement (1,40,CH,A) will be sent to the printer specified in theSORTOFPR statement, to the tape volume specified in the SORTOFTP statement, andto the disk data set specified in the SORTOFDS statement.

3. Hohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aw to Use SyncSort's Data Utility Features3.53

3.54 Programmer'sGuide

Chapter 4.JCL and Sample JCL/Control Statement

's job control statements follow the standard operating system conventions de-scribed in the MVS job control language manuals.Each program application thereforerequires a JOB statement, an EXEC statement, and a DD (data definition) statement forevery data set used.(The single exception to this is the dynamic allocation of work filesvia DYNALLOC or DYNATAPE.)The inclusion and coding requirements of particular jobcontrol statements depend on such factors as whether SyncSort is program-invoked orinitiated directly, whether any exits are coded, and, of course, whether the sorting tech-nique requested is Disk Sort, MAXSORT, PARASORT or Tape Sort.

aspects of program initiation which are specific to the sort/merge (such as the dedi-cated DD names SORTIN and SORTOUT) http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aare documented in this chapter.For completecoding instructions, refer to an MVS JCL reference manual.

following table summarizes Disk Sort's DD statement requirements.

4. JCL and Sample JCL/Control Statement Streams4.1

Disk Sort DD Statements

//STEPLIB DD

//JOLIB DD

//SYSOUT DD

//SORTIN DDInstructs operating system to look for the sort program in aspecified data set.Message data set. Required unless all messages are routed toconsole.SORT input data set. Required unless there is an E15.Ig-

if the invoking program supplies an inline E15 exit

; optional if the MODS statement activates an E15 exit

.

input data set. Required unless there is an E32.

data set. Required unless there is an E35.Ignored if

invoking program supplies an inline E35 exit routine;

if the MODS statement activahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ates an E35 exit routine.

output data sets.One required for each FILES or

specification.

data set of records eliminated by the SUM control

.Required when the XSUM parameter is specified.

work area definition. Required unless incore sort,

, MERGE, COPY or restarting at a MAXSORT

breakpoint.

statement data set. Required unless the invoking

supplies the address of a 24-bit or a 31-bit extended

list.

to override PARM or control statement information.

data set. Required for Checkpoint-Restart.

if user exits are in SYSIN.

if user exits are to be linkage-edited at execution

.//SORTINnn DD//SORTINn DD//SORTOUT DD//SORTOFxx DD//SORTOFx DD//fname//SORTXSUM DD//SORTWKnn DD//SORTWKn DD//SYSIN DD//$ORTPARM DD//SORTCKPT DD//SORTMODhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aS DD//SYSLIN DD//SYSLMOD DD

//SYSPRINT DD

//SYSUT1 DD

//ddname DDRequired for exits unless the exit is inline in

/JOBLIB/STEPLIB or in SYSIN.

.2 Programmer'sGuide

EXEC Statement

EXEC statement is required in order to indicate to the operating system that the job

a sort/merge application.For a Disk Sort, the format of the EXEC statement is as

.  PGM=SYNCSORT    PGM=SORT //stepnameEXEC   PGM=IERRCO00  [ ,PARM='...' ]  PGM=IGHRCO00    PGM=ICEMAN

.Disk Sort EXEC Statement Format

use a sort cataloged procedure, omit PGM= and specify the appropriate procedure

.

PARM parameter may be used to pass the sort/merge program a variety of keyword

, modifying it to meet the needs of the individual application.

MAXSORT, PARASORT and Tape Sort

format of the EXEC statement varihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aes with the sorting technique chosen.The

and PARASORT PARM options are used to request the MAXSORT or

sorting technique; these PARMs are compatible with any of the PGM names

Disk Sort.A Tape Sort application, on the other hand, requires a PGM name of SORT,

, IGHRCO00, or ICEMAN.When PGM=SYNCSORT is used, SORTWK must

assigned to disk.The set of available PARM options is also dependent on sorting

.Refer to “Chapter 5.PARM Options” for a description of the available options.Coding Conventions for DD Statements

following table summarizes the standard coding conventions for DD statements as

relate to the sort/merge program.For more detailed information, refer to an MVS

control language manual.

4. JCL and Sample JCL/Control Statement Streams4.3

Parameter

/DSNSubparameterRequired?To accehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ass a labeled data set (e.g., SORTIN,

) or to keep or catalog the data set

created (e.g., SORTOUT,

).

not required for disk or standard la-

tape input.DCB

, LRECL,

BLKSIZETo override the values in the data set labelof an old data set; to override the values in

first SORTIN or SORTINnn file for a

data set.

indicate ASCII input and output.

an input file that is not cataloged or

; for a new data set

a new DASD data set.

an input file that is not cataloged or

; for a DASD output data set to be

or passed.

override (1,SL).

override (NEW,DELETE).OPTCD andBUFOFFUNITSPACEVOLUME/VOLLABELDISP

/JOBLIB DD Statement

SyncSort has been installed in a private user library or in a test library, a STEPLIB

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a JOBLIB DD statement is required.The sample DD statement below instructs the

system to look for the sort in a partitioned data set named SYNCTEST.

//STEPLIB DDDSN=SYNCTEST,DISP=SHR

.Sample STEPLIB DD Statement

DD Statement

defines the data set for SyncSort messages.

.4 Programmer'sGuide

//SYSOUT DDSYSOUT=A

.Sample SYSOUT DD Statement

the SYSOUT DD statement is omitted, any message routed to it will be diverted to the

.Omitting the SYSOUT DD statement and setting the MSG=SC PARM (critical

to the console, all messages to the printer), for example, will result in all mes-

being sent to the console.

DD Statement

SORTIN DD statement defines the data set to be sorted or copied.(The input file for

merge application is defined by the SORTINnn DD statement.)http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aIt is required for all

except those where an E15 exit (COBOL Input Procedure) provides all the input

.

SORTIN file must have physical sequential or extended sequential organization or

a member of a partitioned data set or PDSE.It may reside on any device supported

BSAM or VSAM and if it is a VSAM data set, may be key-sequenced, entry-sequenced

relative record.SORTIN data sets may also be BatchPipes/MVS pipes or HFS data

.DCB information need not be supplied for a disk or standard labeled tape file.Any

the information accessed from a standard label can be overridden by coding the ap-

DCB parameter in the JCL.

maximum record lengths supported are 32,760 bytes for fixed-length records and

,767 bytes for variable-length records.

default SyncSort does not accept an uninitialized SORTIN data set and willhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a terminate

with a WER400A message.An uninitialized data set is one that has been

created but never successfully closed.The UNINTDS PARM or installation option

be used to change SyncSort's default mode of processing to accept an uninitialized

data set and process it as an empty file.See “UNINTDS” on page 5.29.//SORTIN DD

// DSN=SALESIN,DISP=(OLD,KEEP),UNIT=TAPE,VOL=SER=123456

.Sample SORTIN DD Statement

this example, the data set to be sorted/copied is named SALESIN.It resides on one

of tape whose volume serial number is 123456.SALESIN is the first data set on that

and has a standard label.

access a SORTIN data set that resides in hiperbatch use the HBSI PARM. For more

about HBSI see “Chapter 5.PARM Options”.

4. JCL and Sample JCL/Control Statement Streams4.5

Concatenatihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ang Input Data Sets

SORTIN file may consist of concatenated data sets, up to the limit supported by the

system.

must determine one set of DCB characteristics to use for reading all data sets

the concatenation.The following rules apply to the DCB characteristics:

When the first data set is fixed length (RECFM=F, FB, FBS), all subsequent data sets

be fixed length and have the same LRECL.

the first data set is variable length (RECFM=V, VB, VS, VBS), all subsequent

sets must be variable length.

variable length data sets, the LRECL of the first data set is used except for the

situations:

The LRECL of a subsequent data set is used if that LRECL is the largest found

is available at sort initialization.An LRECL is available at initialization if

is specified on a SORTIN DD statement or exihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asts in the label of a SORTIN disk

set.

record length specified via the L1 value on the RECORD control statement is

if it is the largest record length found.

For both fixed and variable length data sets, the BLKSIZE of the first data set is used

the BLKSIZE of a subsequent data set is the largest found and is available

sort initialization.A BLKSIZE is available at initialization if it is specified on a

DD statement or exists in the label of a SORTIN disk data set.

following shows sample JCL for concatenating input data sets://SORTIN DD

//

//

// DD

//

//

// DD

//

//

.DSN=AUGUST.SALES,DISP=(OLD,KEEP),UNIT=3390,VOL=SER=DISK1,DCB=(LRECL=200,RECFM=VB,BLKSIZE=7404)DSN=JUNE.SALES,DISP=(OLD,KEEP),UNIT=TAPE,VOL=SER=123456,LABEL=(2,SL),DCB=(LRECL=200,RECFM=V,BLKSIZE=8004)DSN=JULY.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSALES,DISP=(OLD,KEEP),UNIT=TAPE,VOL=SER=654321,LABEL=(1,SL),DCB=(LRECL=100,RECFM=VB,BLKSIZE=8004)Sample Disk and Tape Data Set Concatenation to SORTIN

the preceding example, one disk and two tape data sets have been concatenated. Any

of these data sets could be presented first. Position is not dependent upon BLKSIZE

LRECL.If the LRECL or BLKSIZE cannot be determined at SORT initialization, the

data set must carry the largest LRECL or BLKSIZE of the the concatenation.Typ-

.6 Programmer'sGuide

ically the LRECL or BLKSIZE cannot be determined when the input consists of concat-

tape data sets and the JCL lacks a DCB specification.

Large Input Data Sets

MAXSORT technique is recommended for sorting very large amounts of data when

work space is limited.With this technique, SORTWK requirements are independent

SORTIN sihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aze; thus, regardless of the size of the file, it can be sorted by one sort pro-

using disk work files.MAXSORT's breakpoint/restart capability breaks the over-

sorting application into smaller individual sorts; high priority jobs can execute

these smaller sorts without forcing any data to be resorted.See “Chapter 9.

”.

Elapsed Time for SORTS with Multi-volume or Concatenated TapeSORTIN

PARASORT technique can be used to improve elapsed time performance of sorts that

multi-volume or concatenated tape SORTIN data sets.See “Chapter 10.

” on page 10.1.

or SORTINn DD Statement

and SORTINn DD statements are used to define the input to a merge appli-

.(Use the SORTIN DD statement to define the data set to be sorted or copied.)

or SORTINn DD statements are required for all merhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1age applications unless

E32 exit supplies the input data.SORTINnn and SORTINn data sets may be

/MVS pipes or HFS data sets.

is possible to merge up to 100 data sets.Each input data set is specified on a

or SORTINn DD statement.The valid range for n is 0 through 9; for nn, 00

99. If both SORTINx and a SORTIN0x are specified, they are treated as dupli-

and only the first definition is processed. Each file must receive a different number.

may be skipped or used out of order. There are no restrictions as to which input

are to receive which numbers.

input data set must have the same RECFM, and the records in each file must be

to be sorted in the desired sequence.

default, SyncSort does not accept an uninitialized SORTINnn or SORTINn data set

will terminate processing with a WER400A meshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asage.An uninitialized data set is one

has been newly created, but never successfully closed. The UNINTDS PARM or in-

option can be used to change SyncSort's default mode of processing to accept

uninitialized input data set and process it as an empty file.See “UNINTDS” on page

.29.

4. JCL and Sample JCL/Control Statement Streams4.7

//SORTIN17

//

//SORTIN01

//

//SORTIN24

//

// DDDDDDDSNAME=BRANCHA.FICA,VOL=SER=131313,DISP=OLD,UNIT=3480DSNAME=BRANCHC.FICA,VOL=SER=242424,DISP=OLD,UNIT=3390DSNAME=BRANCHB.FICA,VOL=SER=121212,DISP=OLD,UNIT=3400-3,LABEL=(,NL),DCB=(RECFM=FB,LRECL=80,BLKSIZE=400)

SORTINnn DD Statements (Merge)Figure143.

this example, the DCB information for the first two of the three files to be merged is

by the file labels.In order for the merge to execute,these files musthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a have a

of F or FB, as indicated by the third file's RECFM value.

, SORTOFxx, SORTOFx and SORTXSUM DD Statements

SORTOUT, SORTOFxx, SORTOFx and SORTXSUM DD statements are used to de-

one or more output files.The FNAMES parameter of the OUTFIL control statement

also specify DD names of output files.All output is directed to SORTOUT unless

inline E35 exit (COBOL output procedure) assumes the full responsibility for output

.Records eliminated by SUM processing will be written to the SORTXSUM

statement if the XSUM option was selected on the SUM control statement.These

data sets may be directed to a BSAM or VSAM supported device, to

/MVS pipes or to HFS data sets.

//SORTOUT

//

//

//SORTOF01

//

// DDDDDSN=MASTER.OUT,UNIT=SYSDA,DISP=(NEW,KEEP),SPACE=(TRK,10),VOL=SER=DSK0http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a02DSN=REPORT.OUT,UNIT=SYSDA,DISP=(NEW,KEEP),SPACE=(TRK,10),VOL=SER=DSK002

SORTOUT/SORTOFxx DD StatementsFigure144.

the preceding example, the missing DCB parameters except BLKSIZE will default to

assigned to SORTIN or (for a merge application) to those assigned to the last

in the JCL stream.The DCB BLKSIZE, if missing, will be determined via

-determined blocksize when it is active or from SORTIN if SORTOUT and SORTIN

are the same, otherwise SyncSort will select an appropriate BLKSIZE.

a sort or a merge has an LRECL specified in the output DD JCL that is found to be

than the internally processed record length (determined from SORTIN, the

values of a RECORD statement or an INREC statement), SyncSort will write

.8 Programmer'sGuide

the records to the output data set by truncating the records to the LRhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aECL of that dataset.SyncSort will not truncate records after OUTREC processing.

a sort or a merge that is processing fixed length data has an LRECL specified in theSORTOUT or SORTXSUM JCL that is found to be longer than the internally processedrecord length, SyncSort will pad the output records with binary zeros.This will be donefor SORTXSUM and for SORTOUT when OUTFIL is not in use.It will not be done forany OUTFIL files.

RECFM is specified and the report writing features of the OUTFIL control statementare being used, the RECFMof the output file must include the 'A' subparameter.

a COPY or MERGE, the output file must not be the same as any of the input files.

Allocation

the automatic secondary allocation option was enabled at installation time, requestingsecondary allocation on the output DD statements is not required.This feature auto-matically provides output space for eahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ach of the output files.

place a SORTOUT data set into hiperbatch so that subsequent job steps can access it,use HBSO. For more information about HBSO see the PARM Option chapter in thismanual.

or SORTWKn DD Statement

non-MAXSORT applications, up to 100 data sets may be specified for intermediatestorage when sorting.(MAXSORT, which is recommended for large sorting applications,is limited to 32 SORTWK data sets.)Each work file carries a SORTWKnn or SORTWKnname, with nn a two-digit number between 00 and 99 and n a number from 0 to 9.Thespecifications of SORTWK0 through SORTWK9 are treated as synonyms of SORTWK00through SORTWK09.Each SORTWKnn or SORTWKn must be allocated on a single unitand a single volume.

Sorts may feature any of the following devices:2305, 3330, 3330-11, 3340, 3344,3350, 3375, 3380, 3390, and 9345.When device types are mixed, each device is used tofull capacity.Note thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahat although SORTWK space can be allocated in blocks, tracks, orcylinders, allocating in cylinders will yield optimal performance.The CONTIG option ofthe SPACE parameter should be avoided since it may delay allocation and offers no per-formance advantage.

SORTWKnn DD statement in the following example establishes a primary allocationof 20 cylinders of work space.//SORTWK02 DD UNIT=3380,SPACE=(CYL,20)

SORTWKnn DD Statement for Disk SortsFigure145.

4. JCL and Sample JCL/Control Statement Streams4.9

Secondary Allocation

is no need to specify RLSE and a secondary allocation value on the SORTWKnnDD statement at installations that have set these defaults at SyncSort installation time.

SORTWKnn DD Statements Necessary?

DD statements are not used for merge or copy applications.They are notrequired for sorts executed using the DYNALLOC option.Provided nhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeither DYNALLOCnor FIELDS=COPY is in effect, it will be necessary to include SORTWK data sets when-ever any of these conditions holds:

INCORE is set to OFF.An E14 or E16 is included.Checkpoint-Restart is specified.The criteria for an incore sort are not met.(See the discussion of incore sorts in

“Chapter 12. Performance Considerations”.)

, OUTREC or OUTFIL is used.

is a VSAM data set.

:Sort applications that use SUM, OUTREC, OUTFIL or VSAM SORTOUT and donot provide JCL SORTWORKs may have DYNALLOC automatically enabled. This willallow the completion of a sort that would have terminated for lack of requiredSORTWORK space.

Tape Sort

Sorts use the following devices for intermediate storage:2400 and 3400 series tapeunits with densities of 800, 1600 and 6250 BPI.Each reel of tape must be full-size (2400feet long).Tape cartridges http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adevices (3480, 3490, 3490E and 3590) may also be used.

intermediate storage is on tape, from 3 to 32 data sets may be specified.TapeSORTWKnn files must begin with SORTWK01 and be numbered consecutively.Whendifferent device types and tape densities are mixed, the lowest density is used to calculatethe capacity of each SORTWK volume.The MAXSORT technique (supporting only diskSORTWK files) is strongly recommended for large sorts.

xxxx in the UNIT parameter of the following example represents the installation-specific name used to define a tape device.

.10 Programmer'sGuide

//SORTWK01  DDUNIT= 2400  3400  xxxx

.SORTWKnn DD Statement Format for Tape Sorts

more information, see “Chapter 11. Tape Sort”.

DD StatementThe data set defined by the SYSIN DD statement contains SyncSort control statements.The SYSIN DD statement is required in order to initiate the sohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art/merge through job con-trol language.

//SYSIN DD *

/*FIELDS=(5,3,CH,A)COND=(12,6,PD,EQ,0)

.Sample SYSIN DD Statement

$ORTPARM DD Statement

data set defined by the $ORTPARM DD statement may contain PARM parametersand any of the sort control statements.

and control statements passed via the $ORTPARM DD statement generallyoverride all others passed, whether the sort/merge is called from a program or initiatedthrough job control language.

$ORTPARM DD record format must be F or FB, and the record length must be http://www.wendangwang.combels are not allowed on $ORTPARM card images.Leading blanks are not re-quired on a PARM card image, but at least one leading blank must precede a sort controlstatement keyword.

$ORTPARM data sets must be formatted in accordance with the following rules:

PARM specifications http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aincluded in the $ORTPARM data sets must be specified before

sort control statement specifications.

4. JCL and Sample JCL/Control Statement Streams4.11

PARMS must be specified without the keyword PARM= and without quotation

.

comma in columns 2-70 of a PARM card image followed by a blank, or a comma

in column 71, may be used to indicate that the next record is part of the current

.However, if the PARM specification is present through column 71, a

character must be specified in column 72 to indicate continuation.

may be included on $ORTPARM card images provided there is a blank

the last PARM specification and the comment.You may continue a comment

placing a continuation character in column 72 if there are no additional PARMs.

this case, the entire next card image will be considerhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed a comment.If additional

will follow the comment, you may continue that comment by coding an as-

(*) in column 1 of the next card image.

:Refer to “Chapter 2.SyncSort Control Statements” for additional formatting re-quirements.

following example of a $ORTPARM data set illustrates the conventions for definingthe $ORTPARM data set.//$ORTPARM DD*

,STOPAFT=500,

=(1,8,PD,A)

.Sample $ORTPARM DD Statement

$ORTPARM data set in the previous example overrides the options set in the asso-ciated invoking program (or job control stream) to sort 500 records from the input file.These will be the first 500 records that meet whatever criteria have been set by the ori-ginal application (which might include, for example, the INCLUDE/OMIT control state-ment).BMSG turns on the WERnnnB message set, so that the processing accorded thehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ase500 records is fully documented.EQUALS preserves the order of equal-keyed recordsfrom input to output.//$ORTPARM DD *

,STOPAFT=500,

FIELDS=(12,4,30,8,38,8),

=PD

=(1,8,PD,A)

.Sample $ORTPARM DD Statement

.12 Programmer'sGuide

The preceding example illustrates how to include control statements more than 80 byteslong; continuation cards are indicated by a blank field following an operand-comma com-bination.//SYSIN DD*

=(1,2,3),

.

.

.

//$ORTPARM DD*

=(3,4,5),

.

.

.

.Sample $ORTPARM DD Statement

this example, the OUTFIL control statement in $ORTPARM overrides the OUTFILcontrol statement in SYSIN for file 3, and adds OUTFIL specifications for files 4 and 5.

$ORTPARM Processing for Year 2000 COBOL Applications

$Ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aRTPARM DD facility is particularly useful for COBOL sorts requiring Year 2000processing of year data with SyncSort's year data formats.The year data formats are notsupported by COBOL.Therefore, when a data format specification needs to be changedfor Year 2000 processing, it is necessary to override SORT control statements generatedby COBOL.The override can be accomplished with a $ORTPARM DD statement.Thefollowing example shows a $ORTPARM DD used for this purpose.

//$ORTPARM DD *

=(10,2,Y2Z,A),CENTWIN=1980

.Sample $ORTPARM DD Statement for Year 2000 Processing

this example, the 2-digit year field (10,2) will have Year 2000 processing applied to itvia the Y2Z year data format and the CENTWIN option.

described in the previous section, multiple sort invocations by the same COBOL pro-gram would require multiple $ORTPARM DD statements, each with the FREE=CLOSEparameter.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahapter 4. JCL and Sample JCL/Control Statement Streams4.13

$ORTPARM DD Processing for Multiple Sort Invocations

SyncSort is to be invoked more than once in the same job step, you may need dif-ferent $ORTPARM DD control data sets for each invocation.For multiple control datasets, define each one in the JCL stream, in the desired order, as a disk data set (or par-titioned data set member) with the FREE=CLOSE parameter added.FREE=CLOSE willcause the first sort $ORTPARM data set to be dynamically deallocated by the first sortexecution, and so forth for each sort execution.The following example shows sample JCLwith two $ORTPARM DD statements: //$ORTPARM DD

//

//$ORTPARM DD

//

.

.

//$ORTPARM DD

//DSN=SORT.OPTIONS(SORT1),DISP=SHR,FREE=CLOSEWILLBE USED BY FIRST SORT EXECUTIONDSN=SORT.OPTIONS(SORT2),DISP=SHR,FREE=CLOSEWILLBE USED BY SECOND SORT EXECUTIONDSN=SORT.OPTIONS(Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aORTn),DISP=SHR,FREE=CLOSEWILLBE USED BY THE nTH SORT EXECUTION

Multiple $ORTPARM DD StatementsFigure152.

will proceed from top to bottom of this $ORTPARM data set list.This se-quence must be maintained in the JCL so that the multiple sorts can read the$ORTPARM data sets in the correct order.

$ORTPARM datasets are available only in a JES2 environment.JES3 does notsupport the specification of multiple DD cards for the same DDNAME.

$ORTPARM DD statement for Tape Sort may include only one 80-byte record, whichin turn may only feature PARMs.$ORTPARM cannot be used to override Tape Sortcontrol statements.

DD Statement

DD statement is only used when the CKPT/CHKPT option is set on theSORT/MERGE control statement, requesting the Checkpoint-Restart feature.Refer to“Chapter 12. Performance Considerations” for an explanation of this feature.

Exithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Routines that Require Link-editing at Execution Time

following DD statements are required whenever an exit routine is to be link-editedat execution time.

.14 Programmer'sGuide

SORTMODS DD Statement

partitioned data set defined must be large enough to contain all the exit routinesentered in SYSIN.For exits not entered in SYSIN, it is necessary to supply DD state-ments defining the libraries in which the routines reside.//SORTMODS DDSPACE=(CYL,(2,,4)),UNIT=SYSDA

.Sample SORTMODS DD Statement

DD Statement

SYSLIN DD statement defines the temporary data set that will contain the linkageeditor control statements created by SyncSort for the exit routine(s).//SYSLIN DDDSN=&amp;&amp;TEMP,UNIT=SYSSQ,SPACE=(TRK,1)

.Sample SYSLIN DD Statement

DD Statement

SYSLMOD DD statement defines the temporary data set that will contaihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an the link-edited exit module(s).//SYSLMOD DD

// DSN=&amp;&amp;TEMP2,UNIT=SYSDA,SPACE=(TRK,(10,5,2))

.Sample SYSLMOD DD Statement

DD Statement

SYSPRINT DD statement defines the message data set for the link-editing of sortexits.

//SYSPRINT DDSYSOUT=A

.Sample SYSPRINT DD Statement

4. JCL and Sample JCL/Control Statement Streams4.15

SYSUT1 DD Statement

SYSUT1 DD statement is used to define the temporary data set used as a work areawhen SyncSort link-edits an exit routine.//SYSUT1 DD

// DSN=&amp;&amp;TEMP3,UNIT=SYSDA,SPACE=(CYL,(5,5))

.Sample SYSUT1 DD Statement

Statements for MAXSORT, PARASORT and Tape Sort

MAXSORT technique is initiated by means of the MAXSORT PARM, and utilizesadditional MAXSORT DD statements (SORTBKPT, SORTOU00, SORTOUnn) andPARMs.With MAXSORT, SORTWK files must behttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a allocated to disk devices.This tech-nique is strongly recommended for very large sorting applications in a limited disk workspace environment.

PARASORT technique is initiated by means of the PARASORT PARM and utilizesadditional PARASORT DD statements (SORTPAR1, SORTPAR2, SORTPAR3,SORTPAR4).PARASORT requires disk SORTWK devices.This technique can improvethe elapsed time of sorting applications that have multi-volume tape SORTIN data sets.Tape Sort is initiated by assigning tape work devices.The use of Tape Sort constrainsthe set of PARMs available to the sort, requires a SORTLIB DD statement, and restrictsthe coding of the $ORTPARM and SORTWKnn statements.

detailed descriptions of these techniques refer to “Chapter 9.MAXSORT”, “Chapter

.PARASORT”, and “Chapter 11. Tape Sort”.

JCL/Control Statement Streams

sample JCL/control statement streams in this section illustrate how to shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apecify sort,merge and copy applications with and without exit routines.An example illustratingmultiple output is also included.Refer to “Chapter 3.How to Use SyncSort's Data UtilityFeatures” for comprehensive examples illustrating the data utility and report writingfeatures. Examples of how to invoke SyncSort from a program, COBOL exit routines,MAXSORTs, PARASORTs and Tape Sorts are provided in the appropriate chapters.

.16 Programmer'sGuide

Sorts without Exit Routines

1//SORTOMIT

//SORT1

//STEPLIB

//SYSOUT

//SORTIN

//

//

//

//SORTOUT

//

//

//

//SORTWK01

//SORTWK02

//SORTWK03

//SORTWK04

//SORTWK05

//SYSIN

/* JOBEXECDD DDDDPGM=SYNCSORT,PARM='STOPAFT=1000'DSN=SORT.RESI.DENCE,DISP=SHRSYSOUT=ADSN=INPUT,UNIT=3490,VOL=SER=012345,DISP=(OLD,KEEP),DCBhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a=(LRECL=100,RECFM=FB,BLKSIZE=32700),LABEL=(1,SL)DD DSN=OUTPUT,VOL=SER=543210,UNIT=3490,DISP=(NEW,KEEP),DCB=(LRECL=100,RECFM=FB,BLKSIZE=0),LABEL=(1,SL)DDSPACE=(CYL,(20)),UNIT=SYSDADDSPACE=(CYL,(20)),UNIT=SYSDADDSPACE=(CYL,(20)),UNIT=SYSDADDSPACE=(CYL,(20)),UNIT=SYSDADDSPACE=(CYL,(20)),UNIT=SYSDADD*FIELDS=(1,8,CH,A)COND=(1,8,CH,EQ,C'JOHNDOE')123456789101112

.

.

.Sample JCL/Control Stream (1)The JOB statement gives SORTOMIT as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed. The

PARM instructs SyncSort to terminate after sorting 1,000 records.

STEPLIB DD statement instructs the system to look for SyncSort in the librarynamed SORT.RESI.DENCE. The DISP indicates that this library may be shared.The SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

SORTIN DD statement gives INPUT as thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae input data set name, specifies a 3490tape unit with the volume serial number 012345.The data set is already in existence.3.4.5.

4. JCL and Sample JCL/Control Statement Streams4.17

The DCB parameter shows an LRECL of 100 bytes, a fixed blocked RECFM, and a32700-byte BLKSIZE.The LABEL parameter shows that INPUT is the first data seton the tape, and that it has a standard label.

.The SORTOUT DD statement gives OUTPUT as the output data set name, and

a 3490 tape unit with the volume serial number 543210.The data set is notin existence yet.

DCB parameter for SORTOUT specifies the same LRECL and RECFM asSORTIN.The BLKSIZE will be selected by System Determined BLKSIZE (SDB) ifactive or by SyncSort if SDB is not active.

.The five SORTWKnn DD statements reserve space on direct access devices for

storage. Twenty cylinders are allocated for each of the fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aive SORTWKnndata sets.

SYSIN DD * statement marks the beginning of the system input stream thatincludes the sort control statements.

SORT control statement specifies that one control field will be sorted on. It be-gins on byte 1 of the record, is 8 bytes long, contains character data, and is to besorted in ascending order.8.9.

.The OMIT control statement eliminates any record with JOHN DOE in its first eight

(i.e., in the sort control key).JOHN DOE records are not sorted and are notincluded in the STOPAFT figure. The EXEC statement's STOPAFT PARM termi-nates the sort after 1,000 (non-JOHN DOE) records have been put into the propersequence.

.The END control statement marks the end of the control statements.

.The delimiter statement marks the end of the SYSIN input stream.

.18 Programmer'sGuide

Example 2//SUMSORT

//

//STEPLIB

//SYSOUT://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apar

//SORTIN

//

//

//

//

//

//SORTOUT

//

//

//SORTWK01

//SYSIN

/* JOBEXECDD DDDDPGM=SYNCSORT,PARM='EQUALS'DSN=SORT.RESI.DENCE,DISP=SHRSYSOUT=ADSN=FEB92,EMPLOYEE.MASTER,UNIT=3490,VOL=SER=135790,DISP=(OLD,KEEP)DDDSN=FEB92.EMPLOYEE.UPDATE,UNIT=3490,VOL=SER=999999,DISP=(OLD,KEEP)DD DSN=MAR92.EMPLOYEE.MASTER,UNIT=3490,VOL=SER=246809,DISP=(NEW,KEEP)DDUNIT=SYSDA,SPACE=(CYL,20)DD*FIELDS=(1,9,ZD,A,10,2,BI,A)FIELDS=(12,4,PD)1234567891011

.

.

.Sample JCL/Control Stream (2)The JOB statement gives SUMSORT as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed.The

PARM interacts with the SUM control statement to preserve the first of aseries of equal-keyed records.

STEPLIB DD statement instructs the system to look for SyncSort in the librarynamed SORT.RESI.DENhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCE.The DISP shows the library may be shared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with class A.

SORTIN DD statements define two concatenated data sets:FEB92.EMPLOYEE.MASTER and FEB92.EMPLOYEE.UPDATE.They are foundon standard labeled 3490 tape units (volume serial numbers 135790 and 999999, re-spectively).These data sets are already in existence.

SORTOUT DD statement gives MAR92.EMPLOYEE.MASTER as the outputdata set name and specifies a 3490 tape unit with the volume serial number 246809.The data set is not in existence yet.

DCB RECFM and LRECL parameters for SORTOUT default to that of the firstSORTIN file.The BLKSIZE will be selected by System Determined BLKSIZE (SDB)if active or by SyncSort if SDB is not active.3.4.5.6.

4. JCL and Sample JCL/Control Statement Streams4.19

7.The SORTWK01 DD statement reserves space on a http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adirect access device for interme-

storage.Twenty cylinders are allocated.Intermediate storage must be pro-vided whenever the SUM control statement is used with a sort.

SYSIN DD statement marks the beginning of the system input stream that in-cludes the sort control statements.

SORT control statement specifies that two control fields will be sorted on.Themajor control field begins on byte 1 of the record, is 9 bytes long, contains zoneddecimal data, and is to be sorted in ascending numerical order.The second, lesssignificant, control field is found in the next two bytes of the record (bytes 10 and 11),is in (unsigned) binary format, and is to be sorted in ascending order.8.9.

.Whenever two records have equal control fields, the sort will attempt to summarize

.If the result of summing the packed decimal data found in the 4-byte fieldbeginning at byte 12 can be contained in four bhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aytes, one of the two records will beretained, the sum stored in bytes 12-15, and the other record will be deleted.TheEQUALS PARM guarantees that the first of the two records will be preserved; thus,if a record from the FEB92.EMPLOYEE.MASTER file has the same key as one fromthe FEB92.EMPLOYEE.UPDATE file, it is the master record which is retained in theoutput file, containing their sum.

.The delimiter statement marks the end of the SYSIN input stream.

.20 Programmer'sGuide

Example 3//SORTSKIP JOB

// EXECPGM=SYNCSORT

//$ORTPARM DD*

=100

//STEPLIB DD DSN=SORT.RESI.DENCE,DISP=SHR

//SYSOUT DDSYSOUT=A

//SORTIN DDDSN=EXPORT.SHIPPING.VOL6,

// UNIT=TAPE,VOL=SER=112233,

// DISP=(OLD,KEEP)

//SORTOUT DD DSN=RECENT.MAJOR.EXPORTS,

// UNIT=TAPE,VOL=SER=332211,

// DISP=(NEW,KEEP)

//SORTWK01 DDSPACE=(CYL,20),UNIT=SYSDA

//SORTWhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aK02 DDSPACE=(CYL,20),UNIT=SYSDA

//SORTWK03 DDSPACE=(CYL,20),UNIT=SYSDA

//SYSIN DD*

=(19,5,CH,A),

,SKIPREC=1000

=(37,4,BI,GE,X'50')

/*

.

.

.

.Sample JCL/Control Stream (3)123456789101112The JOB statement gives SORTSKIP as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed.The $ORTPARM DD statement is used here to initiate a test run of the SORTSKIP

by supplying the STOPAFT PARM to SyncSort.It instructs SyncSort to termi-nate after sorting the first 100 of the records INCLUDE selects from theSKIPREC-edited input file.

STEPLIB DD statement instructs the system to look for SyncSort in the librarynamed SORT.RESI.DENCE.The DISP indicates that this library may be shared.The SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparThe SORTIN DD statement gives EXPORT.SHIPPING.VOL6 as the input data setname.It is found on a standard labeled tape having the volume serial number112233.This data set is already in existence.

SORTOUT DD statement assigns the RECENT.MAJOR.EXPORTS data setname to the output file, and specifies a tape unit with the volume serial number332211.This data set is not yet in existence.The DCB RECFM and LRECL pa-4.5.6.7.

4. JCL and Sample JCL/Control Statement Streams4.21

rameters for SORTOUT default to those of the first SORTIN file.The BLKSIZE willbe selected by System Determined BLKSIZE (SDB) if active or by SyncSort if SDBis not active.

.The three SORTWKnn DD statements reserve space on direct access devices for

storage.Twenty cylinders are allocated for each SORTWK data set.The SYSIN DD statement marks the beginning of the system input stream that in-cludes the sort conthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arol statements.9.

.The SORT control statement specifies that one control field will be sorted on.It be-

on byte 19 of the record, is 5 bytes long, contains character data, and is to besorted according to ascending order.The EQUALS parameter preserves the SORTINorder of records with identical data in these five bytes.The SKIPREC parametereliminates the first 1,000 records of the SORTIN file from consideration; these re-cords are eliminated before the INCLUDE statement takes effect.

.The INCLUDE statement compares the 4 bytes beginning with byte 37 of the record

the hexadecimal literal, which will be padded on the right with binary zeros to theindicated (4 byte) length.The record is eliminated from the sort unless the binarydata in that field is at least as great as the padded constant.The INCLUDE/OMITstatement takes effect after SKIPREC but before STOPAFT.

.The delimiter statement marhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aks the end of the SYSIN input stream.

.22 Programmer'sGuide

A Merge without Exit Routines

4//EDITMERG JOB

//MERGE1 EXECPGM=SYNCSORT

//STEPLIB DD DSN=SORT.RESI.DENCE,DISP=SHR

//SYSOUT DDSYSOUT=A

//SORTIN08 DDDSN=SALES91,UNIT=TAPE,

// VOL=SER=123456,DISP=(OLD,KEEP)

//SORTIN12 DDDSN=SALES92,UNIT=TAPE,

// VOL=SER=654321,DISP=(OLD,KEEP)

//SORTIN03 DDDSN=SALES93,UNIT=3390,

// VOL=SER=DISK11,DISP=SHR

//SORTOUT DD DSN=SALES.PATTERN,UNIT=3390,

// VOL=SER=DISK08,DISP=(NEW,KEEP),

// SPACE=(CYL,5),

// DCB=(LRECL=20,RECFM=VB,

// BLKSIZE=27980)

//SYSIN DD*

=(5,4,ZD,A)

=V,LENGTH=(100,,20)

=(1,8,29,6,12,6)

/*

.

.

.

.Sample JCL/Control Stream (4)1234567891011The JOB statement gives EDITMERG as the jobname.The EXEC shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atatement identifies SYNCSORT as the program to be executed.The STEPLIB DD statement instructs the system to look for SyncSort in the library

SORT.RESI.DENCE.The DISP shows the library may be shared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

data sets are to be merged:SALES91, SALES92 and SALES93.SALES91 andSALES92 are found on standard labeled tapes with the volume serial numbers123456 and 654321, respectively.The DD statement for SALES93 specifies a 3390disk device with the volume serial number DISK11.These three data sets are al-ready in existence, and the disk data set SALES93 may be shared.They are assigneddistinct SORTINnn numbers, as required.4.5.

4. JCL and Sample JCL/Control Statement Streams4.23

6.The SORTOUT DD statement assigns the name SALES.PATTERN to the output data

and specifies a 3390http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a disk device with the volume serial number DISK08.Fivecylinders of primary space have been allocated on this volume.The data set does notyet exist.DCB parameters are provided, preventing them from defaulting to thoseof the SORTIN08 file.

SYSIN DD statement marks the beginning of the system input stream that in-cludes the sort control statements.

control statement specifies one control field. It begins on byte 5 (thefirst data byte of the record since TYPE=V is specified on the RECORD statement)and is 4 bytes long.This field contains zoned decimal data and is to be merged inascending order.

RECORD statement indicates that variable length records are being merged andindicates the record length at various processing stages.The maximum input recordlength is specified as 100 bytes.Since there is no E15, the post-E15 length value isnot coded and so defaults to this figure.The INREC statement reduces http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athis maxi-mum record length to just 20 bytes.7.8.9.

.According to the RECORD control statement, the input record may be 100 bytes long.

INREC statement reduces each record to the 20 bytes crucial to this application:the 4-byte RDW and 4-byte merge control field (i.e., the first 8 bytes of the record),the 6-byte field beginning at byte 29 (the 25th data byte) and the 6-byte field begin-ning at byte 12 (the 8th data byte).As required, the RDW remains in the first fourbytes.The records to be merged are no more than 20 bytes long and contain threefields following the RDW.

.The delimiter statement marks the end of the SYSIN input stream.

.24 Programmer'sGuide

A Copy without Exit Routines

5//COPYNYC JOB

//COPY1 EXECPGM=SYNCSORT

//STEPLIB DD DSN=SORT.RESI.DENCE,DISP=SHR

//SYSOUT DDSYSOUT=A

//SORTIN DDDSN=USA.OUTLETS,UNIT=TAPE,

// VOL=SER=149200http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,DISP=(OLD,KEEP)

//SORTOUT DD DSN=NYC.OUTLETS,UNIT=3390,

// VOL=SER=DISK08,SPACE=(CYL,5),

// DISP=(NEW,KEEP)

//SYSIN DD*

=COPY

=(56,3,CH,EQ,C'NYC')

/*

.

.

.

.Sample JCL/Control Stream (5)12345678910The JOB statement gives COPYNYC as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed.The STEPLIB DD statement instructs the system to look for SyncSort in the library

SORT.RESI.DENCE.The DISP shows the library may be shared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

SORTIN DD statement indicates the file to be copied.The data set name isUSA.OUTLETS, and it is found on the standard labeled tape with the volume serialnumber 149200.The data set is already in existence.

SORTOUT DD statement names http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe copied file NYC.OUTLETS, and specifies a3390 disk device with the volume serial number of DISK08.Five cylinders of primaryspace have been allocated on this volume.The data set does not yet exist, but is tobe kept whether or not the job terminates normally.The DCB RECFM and LRECLparameters for SORTOUT default to that of the first SORTIN file.The BLKSIZEwill be selected by System Determined BLKSIZE (SDB) if active or by SyncSort ifSDB is not active.

SYSIN DD statement marks the beginning of the system input stream that in-cludes the sort control statements.4.5.6.7.

4. JCL and Sample JCL/Control Statement Streams4.25

8.The FIELDS parameter specifies a copy application. This could have been coded as

FIELDS=COPY without affecting program execution.

INCLUDE control statement edits the USA.OUTLETS input file, eliminating allrecords which do not have the character string NYC inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a bytes 56-58.Only 'NYC' re-cords will be copied.9.

.The delimiter statement marks the end of the SYSIN input stream.

.26 Programmer'sGuide

A Sort with an Exit Routine Already Link-edited

6//ONE#EXIT

//STEP1

//STEPLIB

//SYSOUT

//MODLIB

//SORTIN

//

//SORTOUT

//

//

//SORTWK01

//SORTWK02

//SORTWK03

//SORTWK04

//SYSIN

/* JOBEXECDD DDDDDDPGM=SYNCSORT,PARM='MSG=SC'DSN=SORT.RESI.DENCE,DISP=SHRSYSOUT=ADSN=EXIT.E15,DISP=SHRDSN=INPUT,UNIT=3390,VOL=SER=ABCDEF,DISP=(SHR)DD DSN=OUTPUT,UNIT=3390,VOL=SER=GHIJKL,SPACE=(CYL,10)DISP=(NEW,KEEP,DELETE)DDUNIT=SYSDA,SPACE=(CYL,20)DDUNIT=SYSDA,SPACE=(CYL,20)DDUNIT=SYSDA,SPACE=(CYL,15)DDUNIT=SYSDA,SPACE=(CYL,15)DD*FIELDS=(10,25,CH,A,40,10,ZD,D),FILSZ=9000TYPE=V,LENGTH=(1024,,,44,192)E15=(E15,600,MODLIB,N)1http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a234567891011121314

.

.

.Sample JCL/Control Stream (6)The JOB statement gives ONE#EXIT as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed.The MSG

option requests that all messages be routed to the SYSOUT DD statement butonly critical messages be routed to the console.

STEPLIB DD statement instructs the system to look for SyncSort in the librarynamed SORT.RESI.DENCE.The DISP shows the library may be shared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

MODLIB DD statement defines the library in which the exit routine resides;MODLIB is referenced in the MODS control statement.The data set name of thelibrary is EXIT.E15, and the DISP shows that the library may be shared.3.4.5.

4. JCL and Sample JCL/Control Statement Streams4.27

6.The SORTIN DD stahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atement gives INPUT as the input data set name and specifies a

disk with the volume serial number ABCDEF.The DISP parameter indicatesthat the data set is already in existence and may be shared.

SORTOUT DD statement gives OUTPUT as the output data set name andspecifies a 3390 disk with the volume serial number GHIJKL.Ten cylinders of pri-mary space have been allocated on this volume.The DISP parameter shows that thisdata set is not yet in existence.

four SORTWK statements reserve space on four temporary data sets for inter-mediate storage.Twenty cylinders are to be reserved on the first two data sets, fif-teen on the second two data sets.

SYSIN DD statement marks the beginning of the input stream that includes thesort control statements.7.8.9.

.The SORT control statement specifies two sort control fields.The first begins on byte

(data byte 6) of the record, is 25 bytes lhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aong, contains character data, and is to besorted in ascending order.The second control field begins on byte 40 (data byte 36)of the record, is 10 bytes long, has zoned decimal data, and is to be sorted in de-scending order.FILSZ instructs SyncSort to terminate abnormally unless thepost-E15 file contains exactly 9,000 records.

.The RECORD control statement shows that variable length records are being sorted.

first LENGTH value reports that the maximum length of records in the SORTINdata set is 1024 bytes.The comma coded for the second LENGTH value shows thatthis maximum length is not altered by the exit routine.The comma coded for thethird LENGTH value shows that this maximum length is not affected by an E35 orthe INREC/OUTREC statements.The fourth LENGTH value shows that the small-est record in the input data set is 44 bytes long.The fifth LENGTH value shows thatthe record length that occurs most frequently in Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aORTIN is 192 bytes.(This valuewill be used to determine segment size.)

.The MODS control statement states that the exit-type is E15.The name of the actual

routine included at this exit is also E15.The routine requires 600 bytes ofmemory and resides in a library defined on the MODLIB DD statement.Finally, theN indicates that link-editing of the routine has already been performed.

.The END control statement marks the end of the control statements.

.The delimiter statement marks the end of the SYSIN input stream.

.28 Programmer'sGuide

A Sort with an Exit Routine to be Link-edited

7//LINKEXIT JOB

//STEP EXECPGM=SYNCSORT

//SYSOUT DDSYSOUT=A

//SORTIN DDDSN=IN.FILE.JANUARY,

// UNIT=TAPE,VOL=SER=135790,

// DISP=OLD,DELETE),

// DCB=(LRECL=200,RECFM=FB,

// BLKSIZE=4000),LABEL=(2,SL)

//SORTOUT DD DSN=OUT.FILE.FEBRUARYhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,

// UNIT=TAPE,VOL=SER=097863,

// DISP=(NEW,KEEP),LABEL=(1,SL)

//SORTMODS DDDSN=A.PART.DATA.SET,DISP=OLD

//MODLIB DDDSN=EXIT.NO.ONE,DISP=SHR

//SYSLMOD DD DSN=&amp;&amp;LINK,UNIT=SYSDA,

// SPACE=(CYL,(1,1,1))

//SYSLIN DDDSN=&amp;&amp;TEMP,UNIT=SYSSQ,

// SPACE=(TRK,1)

//SYSPRINT DDSYSOUT=A

//SYSUT1 DDUNIT=SYSDA,SPACE=(CYL,(1,1))

//SYSIN DD*

=(20,30,CH,A),

=(SYSDA,6)

=F,LENGTH=200

=(EXIT1,600,MODLIB,N),

=(EXIT2,500,SYSIN)

=(1,10,ZD)TOTALBALANCE

FOR JANUARY BEGIN FEBRUARY

.

.

.

deck EXIT2 for E35 exit routine

.

.

.

/*

.

.Sample JCL/Control Stream (7)12345678910111213141516171819The JOB statement gives LINKEXIT as the jobname.

4. JCL and Sample JCL/Controhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1al Statement Streams4.29

2.

.The EXEC statement identifies SYNCSORT as the program to be executed.The SYSOUT DD statement assigns the SyncSort messages to the output device as-

with SYSOUT class A.

SORTIN DD statement gives IN.FILE.JANUARY as the input data set name,and specifies a tape unit with the volume serial number 135790.The DISP param-eter shows that the data set is already in existence.

DCB parameter shows an LRECL of 200 bytes, a fixed blocked RECFM, and a4000-byte BLKSIZE.The LABEL parameter shows that IN.FILE.JANUARY is thesecond data set on the tape, and that it has a standard label.4.

.The SORTOUT DD statement gives OUT.FILE.FEBRUARY as the output data set

, and specifies a tape unit with the volume serial number 097863.The DISPparameter shows that the data set is not in existence yet.

DCB RECFM and LRECL parameters for SORTOUT defaulthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a to that of the firstSORTIN file.The BLKSIZE will be selected by System Determined BLKSIZE (SDB)if active or by SyncSort if SDB is not active.The LABEL parameter shows thatOUT.FILE.FEBRUARY is to be the first data set on the tape, and will have astandard label.

.The SORTMODS DD statement defines the partitioned data set that will contain the

routine object module that has not been link-edited and is being included in theSYSIN data stream.The DISP shows the data set may not be shared.

MODLIB DD statement defines the partitioned data set in which the alreadylink-edited exit routine resides.(Note MODLIB is referenced on the MODS controlstatement.)The data set name of the exit library is EXIT.NO.ONE.The DISP showsthe data set may be shared.

SYSLMOD DD statement defines a temporary data set called &amp;&amp;LINK that willcontain the exit routine after it has been link-edited.A direct access devihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ace will beused with 1 cylinder reserved for primary space allocation, 1 cylinder for secondaryspace allocation, and 1 directory block.

SYSLIN DD statement defines the temporary data set that will contain thelinkage editor control statements that SyncSort will use when link-editing the exit.The name of this data set is &amp;&amp;TEMP.It is to be on any sequential-access devicewith 1 track reserved if the data set is allocated to disk.7.8.9.

.The SYSPRINT DD statement defines the data set on which the linkage editor will

its messages.Whatever device is assigned to SYSOUT=A will be used.

.The SYSUT1 DD statement defines the temporary data set that will be used as a

area by the linkage editor.It is to be on a direct access device with 1 cylinderof primary space allocated, and 1 cylinder of secondary space allocated.

.30 Programmer'sGuide

12.The SYSIN DD statement mahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arks the beginning of the input stream that includes the

control statements and also the object deck of the exit routine to be link-edited.

.The SORT control statement shows that one control field will be sorted on.It begins

byte 20 of the record, is 30 bytes long, contains character data, and is to be sortedaccording to ascending order.

DYNALLOC parameter specifies that 6 direct access areas are to be reserved forsortwork data sets.

.The RECORD control statement shows that fixed length records are being sorted.

LENGTH parameter gives 200 bytes as the length of the records at input time,and, by not specifying values for l2and l3, implicitly states that the length of theserecords will not be changed during the sort.

.The MODS control statement shows that the first exit-type is E15.The name of the

for this exit is EXIT1.It will take 600 bytes in mainhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a storage, resides in a li-brary defined on the MODLIB DD statement, and has already been link-edited.

second exit-type is E35.The name of the routine for the exit is EXIT2, and itwill take 500 bytes in main storage.The object deck for the routine is to be includedin the SYSIN portion of the job stream, and, because of the absence of a letter in thelast subparameter position for this group, the sort assumes that the routine requireslink-editing and will be link-edited together with any other routines for this phase.

.The SUM control statement's FIELDS parameter identifies one summary field.It

on byte 1 of the record, is 10 bytes long, and has zoned decimal data.The restof the statement is a comment.

.The END control statement marks the end of the control statements and also con-

a comment.

.The EXIT2 object deck to be link-edited is included after the END statement in http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe

stream.

.The delimiter statement marks the end of the SYSIN input stream for the sort.

4. JCL and Sample JCL/Control Statement Streams4.31

Multiple Output Files

8//MULTOUT

//

//STEPLIB

//SYSOUT

//SORTIN

//

//SORTOUT

//

//

//SORTOFDS

//

//

//SORTWK01

//SORTWK02

//SORTWK03

//SYSIN

/* JOBEXECDD DDDDPGM=SYNCSORTDSN=SORT.RESI.DENCE,DISP=SHRSYSOUT=ADSN=SALES.RECORDS,VOL=SER=DISK1,DISP=SHRDD DSN=SORTED.SALES.RECORDS,UNIT=TAPE,VOL=SER=112233,DISP=(NEW,KEEP)DDDSN=DOMESTIC.SALES.RECORDS,VOL=SER=DISK8,DISP=(NEW,KEEP),SPACE=(CYL,40),UNIT=SYSDADDSPACE=(CYL,20),UNIT=SYSDADDSPACE=(CYL,20),UNIT=SYSDADDSPACE=(CYL,20),UNIT=SYSDADD*FIELDS=(10,12,BI,A)FILES=OUT,INCLUDE=ALLFILES=DS,OMIT=(62,3,CH,NE,C'USA')12345678910111213

http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.

.

.

.Sample JCL/Control Stream (8)The JOB statement gives MULTOUT as the jobname.The EXEC statement identifies SYNCSORT as the program to be executed.The STEPLIB DD statement instructs the system to look for SyncSort in the library

SORT.RESI.DENCE.The DISP parameter shows that the library may beshared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

SORTIN DD statement gives SALES.RECORDS as the input data set name, andspecifies a disk with the volume serial DISK1.The DISP parameter indicates thatthe data set is already in existence and may be shared.

SORTOUT DD statement names one of the output sorted filesSORTED.SALES.RECORDS, and specifies a tape device with volume serial number4.5.6.

.32 Programmer'sGuide

112233 for storage.The DISP parameter indicates that the data set does not yetexihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ast, but it is to be kept whether or not the job terminates normally.

.The SORTOFDS DD statement names a second sorted output file

.SALES.RECORDS, and specifies a disk device with volume serial num-ber DISK8 for storage.Forty cylinders of space have been allocated on this volume.The DISP parameter indicates that the data set does not yet exist, but is to be keptwhether or not the job terminates normally.

three SORTWK DD statements reserve space on direct access devices for inter-mediate storage.Twenty cylinders are allocated for each of the three SORTWK datasets.

SYSIN DD statement marks the beginning of the input stream that includes thesort control statements.8.9.

.The SORT control statement specifies that one control field will be sorted on.It be-

on byte 10 of the record, is 12 bytes long, contains unsigned binary (BI) data andis to be sorted according to ascendinhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ag order.

.The first OUTFIL control statement is associated with the SORTOUT DD statement.

INCLUDE parameter specifies that all input records are to be included in thisoutput file.

.The second OUTFIL control statement is associated with the SORTOFDS DD state-

.The OMIT parameter specifies that records which do not contain &quot;USA&quot; inbytes 62, 63 and 64 are not to be included in this file.

.The delimiter statement marks the end of the SYSIN input stream.

4. JCL and Sample JCL/Control Statement Streams4.33

4.34 Programmer'sGuide

Chapter 5.PARM Options

options can be specified to provide processing information and to override instal-lation defaults for JCL-initiated and program-invoked applications.

a JCL-initiated application, specify the PARM option(s) on the EXEC statement asfollows: PARM='option,...'

.PARMhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Parameter Format

a program-invoked application, specify the PARM option(s) in a $ORTPARM DD dataset. Omit the keyword PARM= and the single quotes.PARM options for a JCL-initiatedapplication can also be specified in a $ORTPARM data set.

MAXSORT PARMs

MAXSORT feature, designed for large sorting applications, is initiated by theMAXSORT PARM.The following additional PARMs can be specified for a MAXSORTapplication:BKPTDSN, DYNATAPE, MAXWKSP, MINWKSP, NODYNATAPE, RE-START, SORTSIZE, SORTTIME and TAPENAME.These PARMs are described in“Chapter 9.MAXSORT”.

5. PARM Options5.1

PARASORT PARM

PARASORT feature, designed to reduce elapsed time for multi-volume and/or con-catenated tape SORTIN sort applications, is initiated by the PARASORT PARM.Foradditional information on PARASORT, see “Chapter 10.PARASORT”.

Tape Sort PARMs

following additionahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1al PARMs can be specified for a Tape Sort: OSCL, BALN andPOLY.The CRCX and PEER PARMs are accepted but ignored.These PARMs are de-scribed in “Chapter 11. Tape Sort”.

Rules

are three ways in which options can be specified, though not all options can bespecified in all three ways:

As an installation specificationAs a PARM specificationAs a SORT/MERGE control statement specification.

that there are six options that can be specified as a PARM option or a SORT/MERGEoption.They are:CENTWIN, DYNALLOC, EQUALS/NOEQUALS, FILSZ, SKIPRECand STOPAFT.

an option is specified in more than one way, the following precedence rules apply:

A SORT/MERGE or PARM specification overrides an installation specification.A PARM specification overrides a SORT/MERGE specification except forEQUALS/NOEQUALS.

Option Summary Chart

chart on the following pahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ages lists the PARM options.Underscored PARM options aredelivered defaults which may have been altered at installation time.

.2 Programmer'sGuide

PARM Option Name

Sort, MAXSORT,and PARASORTBalances importance of CPU

, elapsed time, and I/O

for best overall sort

. SeeCPU,

, and IO.Note that

options and BALANCE

all mutually exclusive.

produce WERnnB mes-

.

a sliding (s) or fixed

(f) 100-year window that de-

the century to which

-digit year data belongs.En-

that such data is proc-

correctly as a 4-digit

by SORT/MERGE and

OMIT.Also ena-

OUTREC processing to

a 4-digit year (yyyy)

2-digit year input (yy).

=CPD improves perform-

.

specifhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay whether COBOL

use OS/VS COBOL li-

or VS COBOL II or

/370 libraries.

provide a communication

between exit programs.

change the amount of

in which sort/merge

run.

CPU time at ex-

of other performance

. SeeBALANCE,

, and IO.Note that

options and CPU are all

exclusive.No.Available with Tape Sort?BMSGNo.No.No. CMP=CLC (no data validation)is the http://www.wendangwang.comMAREA/CORE/SIZE=nNoYes.CPUNo.

5. PARM Options5.3

PARM Option Name

Sort, MAXSORT,and PARASORTTo provide a SyncSort SNAP

in the event of a critical

.

provide diagnostic infor-

for certain error condi-

.

the dynamic allo-

of work data sets.

indicate a COBhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOL exit.

elapsed time at ex-

of other performance

. SeeBALANCE,

, and IO.Note that these

and ELAP are all mu-

exclusive.

acts to preserve the

of equal-keyed records.

is not available with

.

special processing for

with record

that exceed SyncSort's

internal limit.

indicate the (actual or esti-

) number of records after

processing (E14, E15,

/OMIT, SKIPREC,

, and Phase 1 SUM).

=n causes sort termi-

if n is incorrect.

and MSG control the

of output messages.

hiperbatch processing

SORTIN data set.

SORTOUT data set

hiperbatch.

permits incore and turn-

shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aorts.No.Available with Tape Sort?DIAGPlus additional diagnostic trace.DYNALLOCE15/E35=COBELAPNo.No.No.Yes.EXTCOUNTNo.FILSZ=n/EnFILSZ=En only. Does not take inputprocessing (E14, E15) into account.FLAGHBSIHBSO/OFFYes.No.No.No. INCORE=OFF is the standard.

.4 Programmer'sGuide

PARM Option Name

Sort, MAXSORT,and PARASORTMinimizes IO activity at ex-

of other performance

. SeeBALANCE,

, and ELAP.Note that

options and IO are all

exclusive.

indicate how to handle I/O

: user abend 999 plus

or SyncSort error mes-

only.

pass HISTOGRM data to

variable length re-

sorts.

causes header line and

statements to be

.

collating based on

environment.

and FLAG control the

of mhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aessages.

change the DD name of the

data set.

change the DCB of the

data set.

=ABE changes return

16 to user abend 16.

override the RLSE operand

the SPACE parameter of

SORTWK DD

(s).

specify the amount of

reserved for the user

the 16-megabyte line.

specify the amount of

reserved for the user

the 16-megabyte line.No.Available with Tape Sort?No. I/O errors generate user abend999 plus dump.L6=n,L7=nNo.Accepted but not processed. NOLISTis the standard for invoked sorts,LIST for JCL sorts.No.Yes.Yes.No. The standard is: DCB=(LRECL=120,BLKSIZE=120,RECFM=U).No. User abend 16 is the standard.No.RENT /nameMSGMSGDDPRINT121RC16=ABE/NORC16RESERVE=n/nKNo.RESERVEX=n/nKNo.

5. PARM Options5.5

PARM Option Name

/TAPEONLYDhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aisk Sort, MAXSORT,and PARASORTAffects VSAM SORTOUTonly.Determines whether excessspace is released.Specifies whether system-determined blocksize should

used to select an optimum

for data sets when

is provided.

whether second-

sort work space is auto-

provided.

indicate that n records

be skipped before the

file is sorted or copied.

is not available for

.

sort or copy at most n re-

that survive input file

(E15,

/OMIT, SKIPREC

.)STOPAFT is not avail-

for PARASORT.

if an uninitialized

or SORTINnn input

should be processed.

the type of validity

to be done when proc-

variable length records.

action to be taken://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ara variable length record

not contain all fields ref-

by INCLUDE or

processing.

the processing of

VSAM data sets pro-

as input to a sort,

, or copy.Available with Tape Sort?No. (Tape Sort does not acceptVSAM output.)No. Excess SORTOUT space is notreleased.No.No. Secondary sort work space is notautomatically provided.No.SKIPREC=nSTOPAFT=nNo.No.No.No.No.

.6 Programmer'sGuide

PARM Option Name

Sort, MAXSORT,and PARASORTSpecifies whether positive

ZD fields will be

to a printable for-

.No.Available with Tape Sort?

PARM Options

option optimizes overall performance by balancing among CPU time, sort elapsed

, and I/O activity to SORTIN, SORTOUT and SORTWK.If you wish to emphasize

performahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ance measure at the possible expense of others, use CPU, ELAP, or IO.See

, ELAP, and IO, below.Note that these options and BALANCE are all mutually

.

be used with Tape Sort.

option enables class B messages.They will appear wherever the MSG PARM option

informational messages are to be routed.

be used with Tape Sort.

5. PARM Options5.7

CENTWIN   CENTWIN =    f

CENTWIN PARM option defines a sliding or fixed 100-year window that determines

century to which 2-digit year data belongs when processed by SORT, MERGE,

, OUTREC or OUTFIL OUTREC control statements.

data formats Y2B, Y2C, Y2D, Y2P, Y2S and Y2Z work with CENTWIN to treat a

-digit year value as a 4-digit year.The year data formats can be specified on several

statements:

SORT/http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aMERGE control statements to correctly collate 2-digit years that span century

.For information on using the date data formats for SORT/MERGE field

, see “CENTWIN Parameter (Optional)” on page 2.111 or “CENTWIN

(Optional)” on page 2.36.

/OMIT or OUTFIL INCLUDE/OMIT control statements for correct

involving year data.For information on using the date data formats for

/OMIT processing, see &quot;Specifying Field-to-Field Standard Comparisons for

Fields&quot; under the heading “INCLUDE/OMIT Control Statement” on page 2.16.

/OUTREC or OUTFIL OUTREC control statements to convert 2-digit years

4-digit printable output.For information on using the date data formats for

processing, see “Converting Year Data with Century Window Processing

INREC, OUTREC or OUTFIL OUTREC” on page 2.84 ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1and “Sample OUTREC

Statements with CENTWIN Processing” on page 2.98.

addition, two date formats, Y2ID and Y2IP, are provided for year conversion with

/OUTREC and OUTFIL OUTREC.These formats work with CENTWIN to expand

2-digit year in packed decimal format to a 4-digit year while maintaining the packed

format in the output field.

ensures that year data spanning centuries will be sequenced correctly.For

, without CENTWIN processing, an ascending sort/merge would sequence the

01 before the year 98.With CENTWIN processing, the 01 field could be recognized

a twenty-first century date (2001) and would thus be sequenced after 98 (1998) for an

sort.

CENTWIN option generates either a sliding or fixed century window, depending on

form of CENTWIN is used:CENTWIN=s or CENTWIN=f.

.8 Prhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aogrammer'sGuide

CENTWIN=s specifies a sliding century window, which automatically advances as

current year changes.

variable s is a number 0 through 100.This value is subtracted from the current

to set a century-window starting point.For example, in 1996 CENTWIN=20

create the century window 1976 through 2075.Ten years later in 2006, the

starting year would slide to 1986 (2006 minus 20 = 1986) and the century

would be 1986 through 2085.

CENTWIN delivered default is s=0, which means the current year is the starting

of a century window.

CENTWIN=f specifies a fixed century window.

variable f is a 4-digit year (yyyy) between 1000 and 3000.For example,

=1976 establishes a fixed starting year 1976 for the century window 1976

2075.This window will not change as the current year changeshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.

century window defined by CENTWIN controls processing of year-data.If a 2-digit

field (indicated by Y2B, Y2C, Y2D, Y2P, Y2S, Y2Z, Y2ID or Y2IP) has a value less

the last two digits of the century window start year, the year field will be treated

a year in the century following the year of the century window.All other 2-digit years

be treated as in the same century as the century window start year.

example, consider the century window 1950 through 2049.The 2-digit year fields

be processed as follows:

-digit Field

Processed as Year2001204919501999

ascending sort of the above sample data would produce output data

the following sequence:

-digit Field

Processed as Year1950199920012049

CENTWIN has been specified on the SORT or MERhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aGE control statement as well as in

PARM field, the PARM specification has precedence.

be used with Tape Sort.

5. PARM Options5.9

CMP  CMP=

option specifies the kind of compare operation to be used for sort/merge control fieldsup to 16 bytes long, bearing the format code PD or ZD.

CMP=CPD is used, ZD fields are PACKed and then compared.Invalid PD datamay cause a system 0C7 abend and program termination.The integrity of fields labelled&quot;ZD&quot; is only guaranteed when they contain valid ZD data.Since the zone bits (the left-most four bits of each byte) are lost during packing, UNPKing the field later restores onlyvalid ZD data to its original state.Leading blanks are transformed to leading zeros andalphabetic character data that packs to a valid PD field is converted to valid ZD data.

=CLC uses the compare logical instruction for all PD and http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aZD control fields.No datavalidation is done and the integrity of the output is maintained.

=CPD is the delivered default for the PARM.The delivered default for VLTEST is1, and is consistent with this default.Changing the VLTEST default from 1 to any evennumber forces the use of CMP=CLC when sorting variable length records.

more detailed information and sample comparisons, see the section “Comparing PDand ZD Control Fields” on page 2.36.

be used with Tape Sort.

COB1COBEXIT=

COBEXIT PARM indicates which libraries COBOL E15 and E35 exit routines shoulduse when they are executed.

=COB1 specifies that COBOL exits should use either OS/VS COBOL librariesor no libraries at all.

=COB2, the delivered default, specifies that COBOL exits should use VSCOBOL II or COBOL/370 libraries.VS COBOL II or COBOL/370 run-time library mod-ules typically requirhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae more main storage than OS/VS COBOL library modules.The

.10 Programmer'sGuide

amount of additional storage depends on VS COBOL II or COBOL/370 installation

.When VS COBOL II or COBOL/370 run-time library modules are used, it may

necessary to account for this additional storage by adjusting the b value of the Exit-

parameter on the MODS statement.

be used with Tape Sort.

COMMAREA(n,x)    COMMAREA(n)   COMMAREA(,x)   COMMAREA

COMMAREA parameter instructs SyncSort to provide an area for communication

exit programs.The size of this area is given as a decimal number n of bytes; x,

character string at most n bytes long, designates the initial value to be stored in this

.Regardless of the value of n, which may be between 1 and 256, x may not exceed

bytes in length.(Whenever x has fewer than n charhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aacters, it will be right-padded with

to a length of n.)If COMMAREA is specified via the EXEC statement, blanks

be included within the string x.However, if COMMAREA is specified via the

$ORTPARM DD statement, intervening blanks are not allowed.In neither case is a right

permitted since it delimits the COMMAREA parameter.

n and x are optional.If either subparameter is specified, it will determine the other:

defaults to the length of x, x defaults to n blanks.If neither x nor n is specified, n de-

to 80 bytes, x to 80 blanks.

is the program default:no area for communication between exit pro-

is provided, although exit routines may still use the 19th word of the save area.

program access to this communication area is described in the discussion of exit

, see “The Exit Communication Area” on paghttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae 7.4.

be used with Tape Sort.

5. PARM Options5.11

PARM CodeCommunication Area

.....

.........

.........

://www.wendangwang.comMAREA(10,DEBUG) COMMAREA(10) COMMAREA COMMAREA(,DEBUG) COMMAREA(80,DEBUG)

.(5blanks)(10blanks)(80blanks)(75BLANKS)Examples: Coding the COMMAREA PARM

n    nK   CORE    nM    = MAX   SIZE    MAX-n   MAX-nK   MAX-nM

option is used to override the installation default for the amount of memory the

/merge is allowed to use.To specify an amount of memory, choose one entry from each

of braces.

that CORE and SIZE are synonymous.Note also that memory specification may

a decimal number of bytes (CORE=n), a decimal multiple of K, where K=1024 bytes

(CORE=nK), or a decimal multiple of M, where M=1048576 bytes (CORE=nM).

simplicityhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a, the following describes only CORE, specified in units of nK.

=nKDefines a maximum memory limit of nK below the 16-megabyte

.

to the sort/merge all the available memory above and be-

the 16-megabyte line.

to the sort/merge all the available memory above and be-

the 16-megabyte line less nK bytes, which is reserved below

16-megabtye line.CORE=MAXCORE=MAX-nK

your systems staff for any installation-specific modifications to the handling of

. For example, &quot;CORE&quot; will be limited if a maximum memory size for SyncSort was

at installation time.

.12 Programmer'sGuide

CPUDEBUGDIAGCPUThe CPU PARM minimizes the CPU time of each sort at the expense of sort elapsed timeand I/O activity.See BALANCE, ELAP and IO.Note that these options and CPU areall mutually exclusive.Cannot be used with Tape Sort.Dhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aEBUGThe DEBUG PARM produces a SyncSort SNAP dump in the event that a critical errorforces the sort to terminate.A SNAP dump produced in this way is of use to a SyncSortanalyst in debugging complex problems.See “What to Do Before Calling SyncSort MVSProduct Services” on page 15.53.Note that the PSW AT ENTRY TO SNAP and generalregisters are useless for debugging.Cannot be used with Tape Sort.

DIAG option turns on both the IOERR=ABE and the RC16=ABE options (see theseoptions for explanations).When specified for a Tape Sort, DIAG also turns on a diag-nostic trace and causes system ABEND 0C1 in the event of an I/O error.

5. PARM Options5.13

DYNALLOC  DYNALLOC        d  (nn,mm)     =  (d, n ,RETRY=     [,SC=s])        OFF      OFF

requests the dynamic allocation of SORTWK data sets on device type d.

the device type either as a decimal number (e.g., 3380) or bhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay the system generic

(e.g., SYSDA).Any disk device accepted for a SORTWK DD statement can be

.Note that VIO is not accepted as a unit device.

that the DYNALLOC parameter may be used alone, without any subparameters.

this case, the DYNALLOC installation default settings are used.

MAXSORT applications, n is the number of SORTWK data sets that will be allocated.

many as 32 SORTWK data sets can be specified.The default for n is 3.For

-MAXSORT applications, n can be 1 through 100.This value specifies the number

SORTWK data sets that can potentially be allocated.For values of n that are 31 or

, SyncSort can automatically raise the number to 32 if the application requires.When

is 33 through 100, this value specifies the maximum number of SORTWK data sets that

be allocated.

=OFF can be specified to overrihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ade a DYNALLOC=ON installation default.

data sets allocated by the DYNALLOC parameter normally supplement any

data sets allocated by SORTWKnn DD statements; however, note that there is

installation option to disable DYNALLOC if SORTWKnn DD statements are present.

uses the value specified in the RETRY parameter to request automatic

retry. This facility attempts to avoid a sortwork capacity exceeded condition

disk space is not immediately available to satisfy a DYNALLOC request.When

is specified, SyncSort will automatically retry a specified number of times and

a prescribed interval between DYNALLOC requests.

nn in the first position designates the number of times SyncSort will retry a failed

request. The minimum allowed is 1 and the maximum is 16. The mm in the

position designates the numhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aber of minutes SyncSort waits between each

request. The minimum allowed is 1 and the maximum is 15.RETRY=OFF

be specified to override a RETRY=ON installation default.

an environment where DFSMS manages temporary work data sets, the SC subpa-

specifies a storage class s for SyncSort to use when dynamically allocating

data sets. The storage administrator at your installation defines the names

the storage classes you can specify. Note that an installation written automatic class

.14 Programmer'sGuide

E15E35ELAPselection (ACS) routine can override the storage class you specify. If SMS is not installedor active to manage temporary work data sets, the d device specification will be used inthe SORTWORK dynalloc request.If DYNALLOC has been specified on the SORT control statement as well as in the PARMfield, the PARM specification will take precehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adence.Cannot be used with Tape Sort.E15=COBSpecify the E15=COB option in order to include an E15 exit written in COBOL withoutcoding C on the MODS control statement.Cannot be used with Tape Sort.E35=COBSpecify the E35=COB option in order to include an E35 exit written in COBOL withoutcoding C on the MODS control statement.Cannot be used with Tape Sort.

ELAP PARM minimizes the elapsed time (wall clock time) of each sort at the expenseof CPU time and I/O activity.See BALANCE, CPU and IO.Note that these options andELAP are all mutually exclusive.

be used with Tape Sort.

5. PARM Options5.15

EQUALS   EQUALS

NOEQUALS, there is a random element to the order in which records with identicalcontrol fields will appear in the output.EQUALS guarantees that the first of a series ofequal-keyed records is either first-in (SORT) or from the lowest numbered SORTINnndata http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aset (MERGE).With or without EQUALS, MERGE preserves the order of equal-keyed records within any one data set.

used in conjunction with SUM, EQUALS indicates which of the equal-keyed recordswill be preserved, containing the sum:the record occurring first in SORTIN (for a sort),or drawn from the SORTINnn data set with the lowest nn number (for a merge) willcontain the totaled fields.

EQUALS option can also be specified on the SORT/MERGE control statement.Thespecification on the control statement takes precedence over the specification in thePARM field.

option enables special processing to accommodate applications that have recordcounts that exceed SyncSort's default internal limit.

default, the internal limit on the number of records that can be sorted for variablelength data or for a sort application that uses the EQUALS option is 4,294,967,295 re-cords.Spehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acifying EXTCOUNT increases the internal limit to 140,737,488,355,327 re-cords.Fixed length sorts without EQUALS, and all merges and copies, have automaticsupport for the maximum number of records allowed by the EXTCOUNT parameter.

that additional SORTWK space may be required when specifying the EXTCOUNTparameter with a VL sort or a fixed length sort with EQUALS.The additional SORTWKspace is 2 bytes per record.This amount can add a significant percentage to the SORTWKspace needs if the LRECL of the records is small.(Small LRECLs are typical of files withan extremely large number of records).Therefore, when using EXTCOUNT with a VL

.16 Programmer'sGuide

FILSZFLAGsort or a fixed length sort with EQUALS, insure that the extra SORTWK space will beavailable.Performance will usually be improved if the EXTCOUNT option is not in effect.There-fore, EXTCOUNT should be used only when appropriate to the application.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aIf the record limit is exceeded, SyncSort will issue a critical error message and terminatethe application.Cannot be used with Tape Sort. FILSZ= n     En   This option indicates the actual (FILSZ=n) or estimated (FILSZ=En) decimal number ofrecords to be sorted, taking into account all record additions and deletions due to an E14or E15 exit routine, the INCLUDE/OMIT control statement, the SUM control statementand the SKIPREC and STOPAFT parameters.FILSZ=n instructs SyncSort to terminate with an error message unless exactly n recordsare to be sorted.Since the number of records SUMed in Phase 1 is indeterminate andmay not be reproducible, much less predictable, only the estimated En value should beused if a SUM control statement is present.If FILSZ is specified for a Tape Sort, only the estimated En value may be given.It shouldindicate the number of records in the input file - not taking into account any records tobe added or deleted http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aby an E14 or E15 exit program.The FILSZ option can also be specified on the SORT control statement.The specificationin the PARM field will take precedence over that on the control statement.   FLAG(I)

FLAG(U)

5. PARM Options5.17

This option controls the routing of output messages.The MSG option, which handles

more comprehensively, is explained later in this section.The format of the

option is given below.

FLAG(I) to route all messages to the data set specified by the SYSOUT DD

and only critical messages to the console.(This is the same as the MSG=SC

.)

FLAG(U) to route critical messages only to both the data set specified by the

DD statement and the console.(This is the same as the MSG=CB PARM.)

NOFLAG to route critical messages only to the console, no messages to the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adata

specified by the SYSOUT DD statement.(This is the same as the MSG=CC PARM.)

MVS/ESA (3.1.3), this option turns on hiperbatch processing for SORTIN data sets.

benefit from hiperbatch processing, the SORTIN data set should already reside in

. Although hiperbatch does provide significant improvements in elapsed time,

causes some degree of degradation in other system resources. If you use HBSI and the

data set does not reside in hiperbatch, you may experience some system degra-

while not realizing any of the benefits that accompany hiperbatch processing.

be used with Tape Sort.

MVS/ESA (3.1.3), this option turns on hiperbatch processing for SORTOUT data sets.

benefits only subsequent job steps that utilize hiperbatch to access this data set.

be used with Tape Sorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.

.18 Programmer'sGuide

INCOREIOIOERR      INCORE   INCOR      =    INCORE=ON requests SyncSort to perform an incore or a turnaround sort wheneverpossible, even if DYNALLOC is specified or SORTWKnn data sets are present.This isthe delivered default.With INCORE=OFF, SyncSort will not perform a turnaround sort even if your input datacan be sorted entirely in memory.Specifying INCORE=OFF without supplyingSORTWKnn data sets or requesting the DYNALLOC option results in a critical errorwhen sorting.Cannot be used with Tape Sort.IOThe IO PARM minimizes the the I/O activity of each sort at the expense of sort elapsedtime and CPU time.See BALANCE, CPU and ELAP.Note that these options and IOare all mutually exclusive.Cannot be used with Tape Sort.

IOERR=ABE

IOERR=ABE to receive user abend 999 if an I/O error should occur.This abendwill cause the job step to terminate, producing a diagnoshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atic dump.

5. PARM Options5.19

NOIOERR is the program default.If this option is in effect, SyncSort will, in the event

an I/O error, terminate with either a return code of 16 or a user abend 16, depending

the RC16 option that is used.

be used with Tape Sort.

L6=n

decimal value n of the optional L6 parameter is provided by the HISTOGRM utility

.It indicates the average number of bytes of work space each record will need,

(if present) the l6 parameter of the RECORD control statement.If neither L6

l6 is provided, SyncSort will estimate this value.

is only used for sorting variable length records.It is ignored by Tape Sort, merge, and

applications.

be used with Tape Sort.

L7=n

decimal value n of the optional L7 parameter is provided by the HISTOGRM utility

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arprogram.It indicates the segment length that SyncSort should use for maximum sorting

.(A segment is a fixed length area used to contain all or part of a variable length

.)The L7 value overrides (if present) the l7 parameter of the RECORD control

.If neither L7 nor l7 is provided, SyncSort will estimate this value.

is only used for sorting variable length records.It is ignored by Tape Sort, merge, and

applications.

be used with Tape Sort.

.20 Programmer'sGuide

LISTLOCALE         LIST, the default for the sort/merge program, causes header lines and control statementsto be listed with the SYSOUT data set (in all likelihood, at the printer) for both JCL- andprogram-initiated executions.If NOLIST is specified, the control statements and headerlines will not appear with this data set.Tape Sort accepts but does not process this parameter.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar=

controls cultural environment processing, allowing you to choose an alternativeset of collating rules based on a specified national language.For SORT/MERGE proc-essing, thealternative collating applies to character (CH) fields.For INCLUDE/OMITcomparison processing, thealternative collating applies to character fields andhexadecimal constants compared to character fields.

employs the callable services of IBM's Language Environment for MVS to collatedata in a way that conforms to the language and conventions of a selected locale.A localedefines single and multi-character collating rules for a cultural environment.Numerouspre-defined locales are available.

, the default setting for LOCALE, results in normal EBCDIC collating.

directs SyncSort to use the locale active when SyncSort begins.

is the name of a supplied or user-definhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed locale that is to be active during SyncSortprocessing.A locale name may be up to 32 characters and is not case sensitive.The lo-cale active just before SyncSort processing begins will be restored when SyncSort proc-essing completes.The following is a list of locales provided with the IBM NationalLanguage Resources Feature of LE/370.

5. PARM Options5.21

Locale

_DK

_CH

_DE

_GR

_GB

_JP

_US

_ES

_FI

_BE

_CA

_CH

_FR

_IS

_IT

_JP

_BE

_NL

_NO

_PT

_SE

_TRLanguageCountryDanishGermanGermanGreekEnglishEnglishEnglishSpanishFinnishFrenchFrenchFrenchFrenchIcelandicItalianJapaneseDutchDutchNorwegianPortugueseSwedishTurkish

18.DenmarkSwitzerlandGermanyGreeceUnited KingdomJapanUnited StatesSpainFhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ainlandBelgiumCanadaSwitzerlandFranceIcelandItalyJapanBelgiumNetherlandsNorwayPortugalSwedenTurkeyDefinedLocalesNotes:

.22 Programmer'sGuide

1.Make sure the JCL gives SyncSort access to the library that contains the loadable

routines.For the supplied locales, these are the dynamically loadable routines

the IBM AD/Cycle LE/370 library.For more information, see the IBM publication

Environment for MVS &amp; VM Installation and Customization Guide,

-4817.

locale processing is used for fields specified in a SORT or MERGE control state-

, VLTEST=1 will be forced on in addition to any other VLTEST options in effect.

=1 will cause SyncSort to terminate if a variable length input record does

contain all SORT/MERGE control fields.

locale processing can improve performance compared to external collating

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aes, it should be used only when necessary.Locale processing can significantly

SORT/MERGE and INCLUDE/OMIT performance compared to normal col-

.

E61 exit cannot be used with locale processing.

processing requires additional main storage to support the use of the IBM

Environment facilities.For those jobs that use locale, the below-the-line

size should be increased by 1000K to accommodate the storage needs of the

Environment modules.

cannot be used with Tape Sort.2.3.4.5.6.

AB     AC        MSG =   CC    CP     NO     PC     SC     SP

parameter indicates where SyncSort messages are to be routed.The MSG codes

that the printer is specified for the message data set; if a device other than the

is specified for this data set, messages described as routed to the printer will http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1abe

to this other device instead.

all messages to be routed both to the printer and to the console.causes all messages to be routed to the console, none to the printer.

5. PARM Options5.23

APcauses all messages to be routed to the printer, none to the console.This is the

default.

only critical messages to be routed to the printer and to the console.(This

the same as the FLAG(U) option.)

only critical messages to be routed to the console, no messages to the printer.

(This is the same as the NOFLAG option.)

only critical messages to be routed to the printer, no messages to the console.

no messages to be routed to either the printer or the console.

all messages to be routed to the printer and to the console.

only critical messages to be routed to the console,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a all messages to the printer.

(This is the same as the FLAG(I) option.)

only critical messages to be routed to the printer, all messages to the console.CBCCCPNOPCSCSP

MSGDD =

program default for the DD name of the message data set is SYSOUT.To assign a

DD name, substitute any valid DD name for xxxxxxxx.

this option is specified SyncSort changes its DCB default for the message data set

the following:

=(LRECL=121,BLKSIZE=121,RECFM=FA)

PARM is useful when the application includes a COBOL exit which uses DISPLAY,

, or TRACE instructions.(These macros will otherwise cause conflicts between

.24 Programmer'sGuide

program and sort/merge messages.)An alternative is provided by the MSGDD parame-

, used to change the name of the SyncSort message data set.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparThe SyncSort program default for the message file's DCB is:

=(LRECL=125,BLKSIZE=882,RECFM=VBA)

is automatically implemented for all program-initiated sort/merges.

be used with Tape Sort.

RC16=ABE

delivered default is NORC16; unsuccessful completion of the sort causes a return code

16 to be passed to the operating system or the invoking program.

=ABE will cause the sort to issue user ABEND 16 instead of return code 16.The

step is abnormally terminated without a dump and subsequent job steps are gener-

flushed by the operating system.However, JCL may specify job step(s) to be executed

in the event of an ABEND.

be used with Tape Sort.

RELEASE =

RELEASE=ON (the program default), SyncSort will turn on the RLSE operand in

SPACE parameter of the SORThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aWK DD statements.This will cause unused space to

released from sortwork units during execution time.

RELEASE=OFF to instruct SyncSort to turn off the RLSE operand in the SPACE

of the SORTWK DD statement.In this case, SyncSort will not release unused

from the sortwork units during sort execution.

RELEASE parameter has no effect on program-invoked sorts.

5. PARM Options5.25

Cannot be used with Tape Sort.

n RESERVE =   nK    nM

option reserves a specified amount of memory below the 16-megabyte line for the

.This parameter takes effect only when CORE=MAX is in effect.

memory may be specified as a decimal number of bytes (RESERVE=n), a decimal

of K, where K=1024 bytes (RESERVE=nK), or a decimal multiple of M, where

=1048576 bytes (RESERVE=nM).

be used with Taphttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae Sort.

n RESERVEX =   nK    nM

option overrides the installation value that reserves a specified amount of memory

the 16-megabyte line for the user.This parameter takes effect only when

=MAX is in effect.

memory may be specified as a decimal number of bytes (RESERVEX=n), a decimal

of K, where K=1024 bytes (RESERVEX=nK), or a decimal multiple of M, where

=1048576 bytes (RESERVEX=nM).

be used with Tape Sort.

RESET

.26 Programmer'sGuide

If an output VSAM file was created using the REUSE option, specifying RESET will

VSAM from treating SORTOUT, SORTOFx, SORTOFxx or SORTXSUM as MOD

sets.

be used with Tape Sort.

RLSOUT

the RLSOUT parm is specified and DISP=NEW is specified on the SORTOUT,

, SORTOFxx or SORTXhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSUM DD statements, SyncSort will release all excess

and secondary space from each output DASD file.

is the program default.In this case, SyncSort does not release any excess

on these output files.

be used with Tape Sort.

SDB =      DISKONLY TAPEONLY

SDB parm specifies whether system-determined blocksize should be used to select

optimum blocksize for SORTOUT, SORTOFxx, SORTOFx and SORTXSUM data sets

none is provided. This parameter will automatically provide a blocksize that will

efficiently utilize the space on the SORTOUT device.

=ON enables the use of system-determined blocksize for both tape and new or pre-

allocated but unopened DASD output data sets except in the following conditions:

A blocksize is found in JCL DCB BLKSIZE specification or, in the case of a

=MOD http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atape data set, it is derived from an available tape label.

output file is a VSAM data set.

5. PARM Options5.27

If the output data set is on DASD, the blocksize selected will be based upon the RECFM

LRECL, either specifically provided or determined from the usual analysis of

or RECORD statement attributes. For example, the blocksize selected for a

output data set assigned to a 3380 or 3390 DASD device will represent a size as

to half-track blocking as possible.

the output file is a tape data set, the blocksize will be determined from the RECFM and

in conjunction with the following rules:

RECFM of F or FS: BLKSIZE=LRECLRECFM of FB or FBS and LABEL type is not AL: BLKSIZE=highest multiple of

that is less than or equal to 32760.

of FB and LABEL type is AL: BLKSIZE=highest multiple ofhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a LRECL that is

than or equal to 2048.

of V, VS, D: BLKSIZE=LRECL  4

of VB, VBS: BLKSIZE=32760

of DB: BLKSIZE=2048

SDB=OFF is specified, SyncSort will not use system-determined blocksize.The DCB

, if missing, will be determined from SORTIN if the SORTIN and SORTOUT

are the same, otherwise SyncSort will select an appropriate BLKSIZE.

SDB=DISKONLY is specified, SyncSort will use system-determined blocksize only for

output data sets.

SDB=TAPEONLY is specified, SyncSort will use system-determined blocksize only for

output data sets.

be used with Tape Sort.

SECOND =

=ON is the program default, providing automatic secondary allocation for all

work data sets, even if it has not been specified in the sort work JCL.With

=OFF, secondarhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay allocation is only possible if it has been specified in the sort

JCL.

be used with Tape Sort.

.28 Programmer'sGuide

SKIPRECSKIPREC=n

=n instructs the sort to skip a decimal number n of records beforesorting/copying the input file.The records skipped are deleted from the input file beforeE15 and INCLUDE/OMIT processing is begun.

SKIPREC=n has been specified on the SORT/MERGE control statement as well as inthe PARM field, the PARM specification will take precedence.

is not compatible with a merge application unless using FIELDS=COPY.

be used with Tape Sort.

=n

STOPAFT=n (a decimal number) is specified, at most n records will besorted/copied.These will be the first n records after any input processing due to an E15,an INCLUDE/OMIT statement, or the SKIPREC parameter.

STOPAFT=n has been specified http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aon the SORT/MERGE control statement as well as inthe PARM field, the PARM specification will take precedence.

is not compatible with a merge application, unless using FIELDS=COPY.

be used with Tape Sort.

YES UNINTDS =

5. PARM Options5.29

The UNINTDS parameter indicates how SyncSort should process a non-VSAM uninitial-

DASD SORTIN or SORTINnn data set in a non-SMS environment. An uninitialized

set is one that has been created but never successfully opened and closed for output.

an SMS environment, uninitialized data sets are always processed as valid empty files.

=YES indicates that an uninitialized data set should be processed as an empty

.If an uninitialized multi-volume data set has the DS1IND80 and DS1IND02 flags

in the format-1 DSCB of the first volume and the number of data extents ishttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a non-zero,

will open the data set for output to set an end-of-file mark before the data set

used for input.

=NO indicates that SyncSort should terminate with a WER400A critical mes-

if an uninitialized data set is provided as input on SORTIN or SORTINnn.

be used with Tape Sort.

n     VLTEST=(       )

VLTEST option allows you to do the following when variable length records are

:

Choose the type of record length validity testing to be performed.Choose whether or not to verify the correct sequence of segments in variable

spanned records.

length validity testing may be performed in all types of applications: sort, merge,

, and BetterGener. Segment sequence checking may only be done during sort and

applications.

first subparameter of the VLTEST Phttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aARM is a number n that instructs SyncSort in

type of validity testing to be performed on variable length records.Choosing a validity

instructs SyncSort to terminate with a critical error (outlined in WER027A,

A or WER167A) in the event of an illegal condition.

particular, VLTEST instructs the sort/merge in the handling of &quot;short&quot; variable length

, i.e., records not long enough to contain all of the control field(s) specified in the

/MERGE control statement.The delivered default for VLTEST is 1.

VLTEST is set to an even number, SyncSort will accept short variable length re-

, padding them with binary zeros to the length of the sort key for the sort compare

.In order to prevent system 0C7 abends due to the binary zero padding, the CMP

.30 Programmer'sGuide

VLTESTIPARM is automatically set to CMP=CLC http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ain these cases.The binary zeros are removedfrom the record, restoring it to its original state, as the output record is being written.0**No validity testing of variable length records.1If input record is shorter than control fields, terminate.This is the delivered de-fault.2**If input record is longer than maximum LRECL or l2 value, terminate.3If either or both of tests 1 and 2, terminate.4**If input record is longer than output LRECL or l3 value, terminate.5If input record is shorter than control fields, or longer than output LRECL or l3value, or both, terminate.6**If input record is longer than the maximum input LRECL or l2 value, or longer thanthe output LRECL, or both, terminate.7If input record is shorter than control fields, or longer than input LRECL or l2value, or longer than output LRECL or l3 value, or any or all of these, terminate.The second subparameter allows you to specify whether or not SyncSort should verify thatthhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae sequence of segments is correct in each variable length spanned record during sortand merge applications.ON is the delivered default and signals that the segment se-quence should be verified.If OFF is selected, all illogical record segments encounteredin the input file will be processed as individual records.The second subparameter does not apply during copy applications.Note:If an illegal condition is detected during a validity test and segment sequencechecking is on, message WER182A will be issued.Cannot be used with Tape Sort.** These values force the use of CMP=CLC for variable length input.

=

VLTESTI parameter specifies to SyncSort how to process variable length records that

not contain all specified INCLUDE or OMIT fields. VLTESTI applies to both regular

OUTFIL INCLUDE/OMIT processing.

5. PARM Options5.31

The delivered default of http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a0 instructs SyncSort to terminate if a record does not completely

all INCLUDE or OMIT fields. A WER250A critical error message is generated to

this condition.

VLTESTI=1 is specified, a record that does not completely contain all

/OMIT fields is treated as having failed the comparison. SyncSort will omit the

if INCLUDE is being used or include the record if OMIT has been specified.

VLTESTI=2 is specified, SyncSort will treat comparisons to fields not completely

within the record as false and decide a record's status for inclusion or omission

fields that are available.If all fields are not present, the record will be processed

having failed the comparison.SyncSort will omit the record if INCLUDE is being used

include the record if OMIT has been specified.

be used with Tape Sort.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aEMT  VSAMEMT=

VSAMEMT option specifies the processing of empty VSAM input data sets.

you specify VSAMEMT=YES, an empty VSAM data set will be processed as a legitimate

set containing 0 records, and SyncSort will end with a return code of 0.

delivered default, VSAMEMT=NO, instructs SyncSort to terminate with a WER254A

error if an empty VSAM data set is specified for input.

be used with Tape Sort.

option specifies if positive ZD summation results are to be converted to printable

.ZDPRINT, the default, enables conversion to printable format.NZDPRINT

the conversion.

.32 Programmer'sGuide

This option determines whether the sign byte of a positive summarized ZD field will be

to a printable format.More precisely, the option specifies whether the zone of

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae last digit should be changed from a hexadecimal C to a hexadecimal F.

be used with Tape Sort.

Accepted But Not Processed by Disk Sorts

following parameters are accepted but not processed by disk sorts:BALN, OSCL,

, CRCX, and PEER.

5. PARM Options5.33

5.34 Programmer'sGuide

Chapter 6.Invoking SyncSort from a ProgramProgramming Flexibility vs. Performance

sort/merge can be invoked by an executing program written in COBOL, PL/1 or as-sembler language. However, since most invoked sorts utilize inline exits (typicallythrough the COBOL SORT verb) and so are handicapped by the calling program's I/Otechniques and memory allocations, sort performance may be degraded by this mode ofinitiation. Whenever performance is an important consideration, the sort should be initi-ated through the EXEC job control statement. Additional programming flexibility http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ais pro-vided by exits which can be separately compiled and link-edited. These may be coded inCOBOL, FORTRAN, REXX, and assembler language. Exits may also be written in PL/1provided that SyncSort is invoked by a PL/1 program.

Statements

DD statements included in the Table of DD Statements for Invoked Sort/Merge arethose which may be required when invoking the sort.

6. Invoking SyncSort from a Program6.1

DD Statement

//$ORTPARM DDUsageUsed to override or add to control

or PARMs supplied from

invoking program.

input data set.

input data sets.

area definition. Defines the

storage for a sort.

data set.When not requiredIf no control statements or PARMsare being overridden or added.If there is an E32 exit routine or ifrunning a merge.If there is an E32 exit routine of ifrunning a sort or cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apy.For incore sort, MERGE, COPY, orwhen using DYNALLOC.If there is an E35 exit routine.//SORTIN DD//SORTINnn DD//SORTINn DD//SORTWKnn DD//SORTWKn DD//SORTOUT DD

//SORTOFxx DD

//SORTOFx DD

//SORTXSUM DD

//SORTLIB DD

//SYSOUT DDAlternate output data set(s).Output data set for records deleted bySUM.Contains modules that are required toperform a Tape Sort.Message data set.When no OUTFIL control statementis present.When the XSUM parameter of theSUM control statement is not used.If Tape Sort is not used.When all messages are routed to con-

or are disabled.

.Table of DD Statements for Invoked Sort/MergeInvoking the Sort/Merge from an Assembler Program

invocation is accomplished by means of the ATTACH, LINK, or XCTL macro

.SyncSort control statements are coded as character-string operands of As-

DC operations. http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aThe calling program passes to the sort/merge a pointer containing

address of either a 24-bit or an extended, 31-bit, parameter list. This list contains the

of the control statement images to be used by the sort. It may also contain other

such as the addresses of E15, E32, and E35 exit routines. Note that when

either the 24-bit or the 31-bit parameter list, the control statement images can be

from $ORTPARM.

.2 Programmer'sGuide

Macro Instructions

choice of macro determines the linkage relationship between the calling program andthe sort/merge load module.The linkage relationship established by ATTACH precludesthe use of the Checkpoint-Restart feature; do not code CHKPT/CKPT on theSORT/MERGE control statement when invoking the sort/merge with the ATTACH macro.With XCTL, care must be taken to ensure that the storage area for the paramhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeter list andother sort control information does not reside in the module issuing the macro - XCTLwill delete this module from memory.This problem can be circumvented in two ways.Either (1) place the parameter list and additional control information in the task thatattaches the module issuing the XCTL; or (2) have the module issuing the XCTL macroissue a GETMAIN macro instruction first, and place all of the sort/merge control infor-mation in the main storage area it obtains. None of the above restrictions apply whenusing the LINK macro.

sort/merge DD statements are placed with the JCL of the job step that issues themacro. The EP parameter is specified as SORT whether SyncSort is to be used for sorting,merging, or copying.With ATTACH, the ECB or EXTR is usually required.

the Sort/Merge Control Statements

control statements are introduced by the invoking programs as character oper-ands in DC ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aperations. Although it is generally true that all control statements supportedfor a JCL-initiated Disk Sort/MAXSORT/Tape Sort are available to invoked applications,these exceptions should be noted:

A MODS control statement cannot be used for an E32 exit and is not required for an

or E35 exit. (An E32, E15 and/or E35 exit routine may be coded in line with theinvoking program with their addresses passed to the sort in the parameter list.Ifthe 31-bit parameter list is being used, an E18 and/or E39 exit routine address mayalso be passed.)

MODS control statement is not supported for an invoked Tape Sort.

RECORD control statement is required if an inline E15 exit routine address isprovided. Its LENGTH parameter is required whenever an inline E15 or E35 exitroutine is used.For a full description of record length parameters, see “RECORDControl Statement” on page 2.103.

END control statementhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a is not used.

actual coding of the control statements is the same, except that:

No comments or labels are permitted within the DC operand.Continuation characters are not called for, since the statements are not in card-image

.

6. Invoking SyncSort from a Program6.3

For the 24-bit parameter list, each control statement DC instruction should be labeledand followed by a DC C' ' instruction so that the beginning and ending addresses of thecontrol statement can be referenced in the parameter list.SORTBEG

DC DC DC DC C'C'C'C'SORTFIELDS=(31,5,CH,A)''RECORDTYPE=F,LENGTH=(80,,120)''

.Sample Control Statement Images for the 24-bit Parameter List

that the 24-bit invoking parameter list and pointer word, as well as the controlstatement images, must be below the 16 megabyte line.

in a JCL-initiathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed sort/merge, control statements must begin with at least one blank.For the 31-bit invoking parameter list, the control statement images will be pointed toby the first word of the parameter list and are organized like the control statement imagesfor a 24-bit parameter list.Note, however, that only the first DC instruction requires alabel since only the start and end of the list need be referred to. The control statementsmust be separated by one or more blanks; that is, each control statement must be followedby a blank. A blank before the first statement is optional; however, a blank after eachstatement is required. Labels, comment statements, and comment fields must not becoded. Each control statement, except the last, must have at least one parameter.CARDLEN

DC DCDC DCDCDCEQU0HY(CARDEND-CARDBEG)C'SORTFIELDS=(31,5,CH,A)'C''C'RECORDTYPE=F,LENGTH=(80,,120)'C''*

Control Sthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aatement Images for the 31-bit Parameter ListFigure169.

24-Bit Parameter List

parameter list is used to pass information from the calling program (e.g., the ad-dresses of the DC control statement images) to the sort/merge. For the parameter listused with invoked Tape Sorts, see “Chapter 11. Tape Sort”.

order to pass the parameter list, it is necessary to load the address of a fullword pointerinto Register 1. Code X'80' in the pointer's first byte and the address of the parameterlist's byte count in its last three bytes. The byte count must be located in the last 2 bytes

.4 Programmer'sGuide

of the first fullword entry in the parameter list. It contains the hexadecimal number ofbytes remaining in the list --do not include these 2 bytes in the count.

first seven words of the parameter list are required and must be coded in the exactorder shown. Note that whenever the address http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aof an exit routine is supplied in the sixthor seventh word of the parameter list, that exit may not be specified in the MODS controlstatement image. Parameter list entries following the seventh fullword are optional andcan be specified in any order. All values not specified in the chart as EBCDIC-coded areto be given in hexadecimal notation. For the most part, these are addresses; the endingaddress refers to the blank coded immediately after the control statement in question, asindicated in the Sample Invoked Sort.

6. Invoking SyncSort from a Program6.5

ADDRESS OF POINTERPOINTER(Fullword)X'80'Address of Parmlist Byte Count Fullword Boundary↓

1Byte 2   ↓Byte 3Byte 4

of bytes in following list

'00'

in

address of SORT or MERGE statementEnding address of SORT or MERGE statementBeginning address of RECORD statemhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aentEnding address of RECORD statement

of E15 or E32 exit routine (Zeros if none)

of E35 exit routine (Zeros if none)

'00'

'01'

'02'Main storage valueReserved main storage valueBeginning address of MODS statement

address of MODS statement

'03'

'04'

'05'Beginning address of message DD name to replaceSYSOUTNumber of input files (Use for merge with E32 exit only)Beginning address of DEBUG statement (Not processed)

address of DEBUG statement

'06'Beginning address of ALTSEQ statement

address of ALTSEQ statement

'07'Beginning address of SUM statement

address of SUM statement

'08'Beginning address of INCLUDE/OMIT statement

address of INCLUDE/OMIT statement

.6 Programmer'sGuide

Byte 1

'09'Byte 2Byte 3Byte 4Beginning address of OUTREC statehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ament

address of OUTREC statement

'0A'Beginning address of INREC statement

address of INREC statement

'0B'Beginning address of first OUTFIL statement

address of first OUTFIL statement

. .

.

'0B' . . .Beginning address of nth OUTFIL statement

address of nth OUTFIL statement

'F6'

'F7'

'FD'

'FE'

'FF'Beginning address of translation tableUser exit address constantIMS flagPointer to STAE work area (May code zeros if none)Message option (Code in EBCDIC)

option (Code in EBCDIC)

, OSCL or POLY (Processed Tape Sort only; code in EBCDIC)

, PEER or LIST (Not processed)

name prefix to replace SORT in JCL (Code in EBCDIC)

.The 24-Bit Parameter List

:Empty boxes indicate the contents are immaterial and not examined.Chapter 6. Invohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aking SyncSort from a Program6.7

...

.

.

.

DC

DC

DC1,POINTEREP=SORT14Load address of pointer to parameter listInitiateSyncSortReturn to invoking program2,4Align to last 2 bytes of a wordY(24)Byte count of parameter listA(SORTBEG)Beginning address of sort statementA(SORTEND)Ending address of sort statementA(RECBEG)Beginning address of record statementA(RECEND)Ending address of record statement2F'0'No E15 or E32 indicated. No E35.X'80'Indicates parameter list's pointerAL3(BYTECNT)Address of parameter listC'SORT FIELDS=(1,16,CH,A),SKIPREC=100'C''C' RECORD TYPE=F,LENGTH=80'C''

.Sample Invoked Sort

this example, only the required seven entries appear in the parameter list. The http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ainvokedsort skips the first 100 records in SORTIN, a data set of 80-byte fixed-length records, andsorts the remainder in ascending sequence according to the character data in its first 16bytes.

parameter-list entries may appear in any order after these required seven; thecontents of the first byte of the word signals which optional parameter it is.

invoked merge applications using the 24-bit parameter list, the number of input filesmust be specified on either the X'04' entry or the FILES=n parameter on the MERGEcontrol statement. However, when using the 31-bit parameter list, the number of inputfiles for a merge must be specified on the FILES=n parameter.

Parameters

in

1

'00'Contents of Bytes 2 - 4Indicates how much main storage SyncSort is to use. Code C'MAX'

a hexadecimal number of bytes.

.8 Programmer'sGuide

Optional Parameterhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as

in

1

'01'Contents of Bytes 2 - 4Indicates how much main storage should be reserved for data handl-

by the invoking program during sort execution. SyncSort will use

available main storage less the hexadecimal number of bytes

here. This parameter takes precedence over the X'00' entry

above.

the beginning address of a MODS control statement image. The

3 bytes of the next word must contain the ending address of this

. All exits may be specified in the MODS statement image ex-

for E32 (use entry 6 of the parameter list for this exit). An

/E35 exit is specified in entries 6-7 or in the MODS image, but

in both.

the address of a replacement for the message data set's DD

. Eight characters are used for the name; the first character

be alphabetihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ac.

the hexadecimal number of SORTIN files-required whenever

E32 exit supplies the input to the merge.

accepts the DEBUG control statement parameter but does

process it. Both this fullword (the beginning address of the DE-

statement) and the next (the ending address) are ignored.

the beginning address of an ALTSEQ control statement image.

last 3 bytes of the next word must contain the ending address of

image.

the beginning address of a SUM control statement image. The

3 bytes of the next word must contain the ending address of this

.

the beginning address of an INCLUDE/OMIT control statement

. The last 3 bytes of the next word must contain the ending

of this image.

the beginning address of an OUTREC control statment image.

last 3 bytehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as of the next word must contain the ending address of

image.

the beginning address of an INREC control statment image.

last 3 bytes of the next word must contain the ending address of

image.X'02'X'03'X'04'X'05'X'06'X'07'X'08'X'09'X'0A'

6. Invoking SyncSort from a Program6.9

Optional Parameters

in

1

'0B'Contents of Bytes 2 - 4Gives the beginning address of an OUTFIL control statement. The

3 bytes of the next word must contain the ending address of this

. This parameter may be specified more than once to accommo-

multiple output file specifications.

the address of a 256-byte translation table, used to alter the

sequence. This parameter takes precedence over the

control statement image.

user exit address constant which can be used to http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apass infor-

between the invoking program, an E15 exit, and/or an E35

. SyncSort passes these 3 bytes to an E15 exit at offset 5 in an

parameter list and to an E35 exit at offset 9 in an E35 parameter

. Offset 4 in the E15 parameter list and offset 8 in the E35 pa-

list will initially contain an X'00'.

the first byte is processed, flagging this as an IMS-initiated sort,

variable length records too short to contain all of the

/merge control field(s).

non-zero, these 3 bytes contain the address of a 104-byte STAE

area.

the MSG/FLAG PARM coding. For the MSG option, specify

, AC, AP, CB, NO, PC, SC or SP in bytes 3-4. For the FLAG option,

NOF, (I) or (U) in bytes 2-4. This parameter is coded in

.X'F6'X'F7'X'FD'X'FE'X'FF'

coded in EBCDIC in the entirhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae word turns on the IOERR=ABE and RC16=ABEPARM options.

/OSCL/POLY coded in EBCDIC in the entire word indicates the Tape Sort tech-nique.Ignored by Disk Sort and MAXSORT.

/PEER/LIST coded in EBCDIC in the entire word is accepted but not processedby SyncSort.

with the first character alphabetic or national (do not use DIAG, PEER, CRCX,etc.) represents the DD name prefix to be used in place of SORT in the JCL.

.Optional Parameters for the 24-Bit Parameter List6.10 Programmer'sGuide

Return Codes

the sort terminates, returning control to the calling program, it places a return codein Register 15:

indicates normal termination;indicates an unsuccessful sort.

calling program typically tests the contents of Register 15, branching to the normal-sort or sort-error end of job routine.

6. Invoking SyncSort from a Program6.11

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSample Assembler Invocation Using 24-Bit Parameter List

...

DC

DC

EQU

DC

DC1,PTRWORDLoad address of parameter list pointerEP=SORTInitiateSyncSort15,15Test return codeSORTERRBranch on error conditionSORTOKBranch to normal processing0,4Fullword alignment for pointerX'80'Indicates pointer to parameter listAL3(PARMS)Address of parameter listHUnused first 2 bytes of first parameterYhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a(PARMSEND-PARMSBEG) BytecountofremainingparametersA(SORTBEG)Beginning address of sort statementA(SORTEND)Ending address of sort statementA(RECBEG)Beginning address of record statementA(RECEND)Ending address of record statementF'0'No E15/E32 exit routineF'0'No E35 exit routineX'03'Indicates SYSOUT DD name changeAL3(MSGNAME)Address of SYSOUT DD name replacementX'08'Indicates INCLUDE/OMIT parameterAL3(OMITBEG)Beginning address of OMIT statementA(OMITEND)Ending address of OMIT statementX'07'Indicates SUM parameterAL3(SUMBEG) BeginningaddressofSUMstatementA(SUMEND)Ending address of SUM statementX'0B'Indicates OUTFIL parameterAL3(OUTBEG1)Beginning address of first OUTFIL statementA(OUTEND1)Ending address of first OUTFIL statementX'0B'Indicates OUTFIL parameterAL3(OUTBEG2)Beginning address of second OUTFIL statementA(OUTEND2)Ending address of second OUTFIL statement*End of parameter listC' SORT FIELDS=(1,20,A,35,8,A),' Begin SORT statemenhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at imageC'FORMAT=CH'Continue SORT statement imageC' 'End SORT statement imageC' RECORD TYPE=F'Begin RECORD statement imageC' 'End RECORD statement imageC' OMIT COND=(21,8,PD,EQ,0)'Begin OMIT statement imageC' 'End OMIT statement imageC' SUM FIELDS=(21,8,PD)'Begin SUM statement imageC' 'End SUM statement imageC' OUTFIL FILES=1,'Begin first OUTFIL statement imageC'HEADER1=(50X,''CHANGES'C' TO W-2 FORMS'',//,'C'50X,''JANUARY THROUGH JUNE'C'1993'')'C' 'End first OUTFIL statement image

Assembler Invocation Using 24-Bit Parameter List (Continued)

.12 Programmer'sGuide

OUTBEG2

...DS...BRDS...BRC' OUTFIL FILES=2,'Begin second OUTFIL statement imageC'HEADER1=(19X,''EMPLOYEE'','C'10X,''DEPARTMENTCODE'','C'10X,''CHANGE''),'C'OMIT=(29,4,PD,NE,0)'OMITconditionC' 'End second OUTFIL statement imageCL8'Mhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aESSAGES'SYSOUT DD name replacement0HError routine for unsuccessful sort140HReturnNormal processing for successful sort14Return

.Sample Assembler Invocation Using 24-Bit Parameter List

example sorts fixed length records by the character data in its first 20 bytes and,

two records have identical data in this field, by the character data in bytes 35-42;

fields are collated in ascending order. Note the continuation of the SORT statement

using consecutive DC instructions. There is no special significance to the break

the FIELDS parameter -- a control statement image can be divided at any point in

way.The SORTIN file is edited by the OMIT statement, which will eliminate any

with zero in bytes 21-28 before sorting begins; these 8 bytes constitute the SUM

.SyncSort messages are written to the data set specified by the MESShttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aAGES DD

. Two OUTFIL parameters have been specified, producing multiple output files. The

OUTFIL will receive data from every sorted input record, producing a company-wide

. The second OUTFIL will receive selected data only, as defined by the OMIT con-

, producing a departmental report.

31-Bit Extended Parameter List

extended parameter list allows the sort to interface with invoking programs that may

31-bit addresses or which may use the 31-bit addressing mode (AMODE).

extended parameter list is not supported for Tape Sorts. For the parameter list used

invoked Tape Sorts, see “Chapter 11. Tape Sort”.

the first word of the extended parameter list is required. The high order bit must

zero to identify this as a 31-bit parameter list. The subsequent words of this list are

, and because therehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a is no code in the high order byte, as in the 24-bit parameter

, their positional order must be maintained.Thus, when coding the list be sure to code

6. Invoking SyncSort from a Program6.13

a fullword of zeros when omitting one of the optional parameters. The last parameter

specified in the list must be followed by the 4-byte field X'FFFFFFFF'.

31-bit parameter list has the following format:

d 31-bit address of start of parameter list

↓

0

4

8

12

16

20

24

28

32

36 dmmd0mmBits 1 through 31Address of halfword containing the lengthof control statement images (zeros if none)Address of user E15 or E32 (zeros if none)Address of user E35 (zeros if none)User exits address constant (zeros if none)Address of ALTSEQ translation tablehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a (ze-ros if none)Address of STAE area field (zeros if noSTAE routine)Address of user exit E18 (zeros if none)Address of user exit E39 (zeros if none)Call identifier (C 'nnnn')X'FFFFFFFF'(required)

.31-Bit Extended Parameter List

:d indicates a bit is immaterial and not examined.

following table provides an explanation of the contents of the extended parameter

.6.14 Programmer'sGuide

Address

0Contents(Required) First word of the parameter list. The high order bit must be

to identify this as an extended parameter list. The other 31 bits

the address of a halfword which contains the length of the fol-

control statement images.A value of 0 (zero) represents a null list

control statement images must be supplied through the $ORTPARM

statement.

(Optional) Address of the E15 or E32 exit routine. This address mhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aay point

in memory.The m bit (bit 0) means: 0=Enter the exit with

-bit addressing in effect (AMODE 24); 1=Enter the exit with 31-bit ad-

in effect (AMODE 31).

(Optional) Address of the E35 exit routine. This address may point any-

in memory.The m bit (bit 0) means: 0=Enter the exit with 24-bit

in effect (AMODE 24); 1=Enter the exit with 31-bit addressing

effect (AMODE31).

(Optional) User exit address constant which can be used to pass informa-

between the invoking program, an E15 exit routine, and/or an E35

routine. SyncSort passes these 4 bytes to an E15 exit routine at offset

in an E15 parameter list and/or to an E35 exit routine at offset 8 in an

parameter list.

(Optional) Address of ALTSEQ translation table. It can point anywhere

memory and has a length of 256 bytes.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar(Optional) If non-zero, the address of a 112-byte STAE work area.

(Optional) Address of the E18 exit routine. This address may point any-

in memory.The m bit (bit 0) means: 0=Enter the exit with 24-bit

in effect (AMODE 24); 1= Enter the exit with 31-bit addressing

(AMODE 31).

(Optional) Address of the E39 exit routine. This address may point any-

in memory.The m bit (bit 0) means: 0=Enter the exit with 24-bit

in effect (AMODE 24); 1= Enter the exit with 31-bit addressing

effect (AMODE 31).

(Optional) Four displayable characters that will uniquely identify this

call to SyncSort. (When this parameter is provided, SyncSort

the WER428I message and includes these four characters in the

. This message facilitates correlation of message output when

is called multiple timeshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a by the same program.)

(Required) The last parameter word specified in the list must be

'FFFFFFFF', which indicates end of list. If optional entries are omitted,

end-of-list indicator is moved up to the word immediately after the

specified parameter.

of the Contents of the 31-Bit Extended Parameter List 4 8 12 16 20 24 28 32 36Table23.

:An optional parameter becomes required if a subsequent parameter is to appear.Chapter 6. Invoking SyncSort from a Program6.15

Return Codes

the sort terminates, returning control to the calling program, it places a return code

Register 15:

indicates normal termination;indicates an unsuccessful sort.

calling program typically tests the contents of Register 15, branching to the normal-

or sort-error end of job routine.

following examples demonstrate howhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a to code an extended parameter list. In this ex-

, all exits reside below the 16-megabyte line and should be called with 24-bit

set, except the E35 exit, which should be called with 31-bit AMODE set.

://www.wendangwang.comLINK...DC

,XLISTEP=SORTPoint at Parameter ListInitiateSyncSortA(CNTLCARD)Address of Control Card ImagesA(E15EXIT)Address of E15 ExitA(E35EXIT X'80000000') Address of E35 ExitF'0'User Address ConstantA(ALTSEQ)Address of ALTSEQ

(STAE)Address of STAE Area Field

(E18EXIT)Address of E18 Exit

(E39EXIT)Address of E39 Exit

'FFFFFFFF'End of Parameter List

DC0H

(CNTLLEN)

DCC' SORT FIELDS=(1,16,CH,A)'

' RECORD TYPE=F,LENGTH=80'

EQU *-CNTLCRD2

.Sample Invoked Sort with Both 24-bit AMODE &amp; 31-bihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at AMODE Set

.16 Programmer'sGuide

This next example demonstrates how to code an extended parameter list in which all exits

above the 16-megabyte line and should be called with AMODE 31 set.

...

.

.

.

DC

DC

EQU 1,XLISTEP=SORTPoint at Parameter ListInitiateSyncSortA(CNTLCARD)Address of Control Card ImagesA(E15EXIT X'80000000') AddressofE15ExitA(E35EXIT X'80000000') AddressofE35ExitF'0'User Address ConstantA(ALTSEQ)Address of ALTSEQ Translation TableA(STAE)Address of STAE Area FieldA(E18EXIT X'80000000') AddressofE18ExitA(E39EXIT X'80000000') AddressofE39ExitX'FFFFFFFF'End of Parameter List0HY(CNTLLEN)C' SORT FIELDS=(1,16,CH,A)'C' RECORD TYPE=F,LENGTH=80'*-CNTLCRD2

.Samplhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae Invoked Sort with 31-bit AMODE Set

6. Invoking SyncSort from a Program6.17

Sample Assembler Invocation Using 31-Bit Parameter List

...

EP=E15EXITLoad E15 exit

,E15ADDRStore E15 AMODE address

,XLISTPoint at parameter list

=SORTInitiateSyncSort

,R15Test return code

on error condition

to normal processing

.

.

.

(CARDLEN)Address of control statements

ADDRDCA(0)Address of E15 routine

(0)No E35 routine

(0)User exit address constant

'FFFFFFFF'End of parameter list

HControl statement area

(CARDEND-CARDBEG)Length of character string

'SORT FIELDS=(1,20,A,35,8,A),' Begin SORT image

'FORMAT=CH'Continue SORT image

'RECORD TYPE=F,LENGTH=80 'RECORD image

'http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOMIT COND=(21,8,PD,EQ,0) ' OMIT image

'SUM FIELDS=(21,8,PD) 'SUM image

'OUTFIL FILES=1,'First OUTFIL image

'HEADER1=(50X,''CHANGES'

' TO W-2 FORMS'',//,'

'50X,''JANUARY THROUGH JUNE'

'1992'')'End first OUTFIL image

'OUTFIL FILES=2,'Second OUTFIL image

'HEADER1=(19x,''EMPLOYEE'','

'10X,''DEPARTMENTCODE'','

'10X,''CHANGE'')'

',OMIT=(29,4,PD,NE,0)'End second OUTFIL image

EQU *

routine for unsuccessful sortSORTERRDS0H

.

.

.

Return

DS 0HNormalprocessingforsuccessfulsort

.

.

.

Return

.Sample Assembler Invocation Using 31-Bit Parameter List

example sorts fixed length records by the character data in its first 20 bytes and,

two records have identical data in this field, by the character http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adata in bytes 35-42;

fields are collated in ascending order. Note the continuation of the SORT statement

.18 Programmer'sGuide

image using consecutive DC instructions. There is no special significance to the break

the FIELDS parameter - a control statement image can be divided at any point in

way.The SORTIN file is edited by the OMIT statement, which will eliminate any

with zero in bytes 21-28 before sorting begins; these 8 bytes constitute the SUM

. Two OUTFIL parameters have been specified, producing multiple output files. The

OUTFIL will receive data from every sorted input record, producing a company-wide

. The second OUTFIL will receive selected data only, as defined by the OMIT con-

, producing a departmental report.

6. Invoking SyncSort from a Program6.19

6.20 Programmer'sGuide

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparChapter 7.The Coding and Use of Exit ProgramsWhat Is an Exit?

term program exits refers to the various points in the sort program's executable codeat which control can be passed to a user-written routine.Most exit routines take controlonce for every record being processed, increasing overall execution time and consumingmain storage that would otherwise be used by the sort.Exits should only be coded fortasks which cannot be accomplished with SyncSort control statements.

exits are not allowed to take their own OS or VS checkpoints.

exits are labeled with a 2-digit decimal number, e.g., E35.Except for E61, thefirst digit (1, 2 or 3) refers to the sort/merge phase at which the routine will get control;an E61 routine can take control in Phase 1 or Phase 3.The second digit refers to thenumber of that exit within the phase.Whenever possible, control passes directly fromPhase 1 to Phase 3, skiphttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aping the intermediate merge phase and its associated exits: E21,E25 and E27.

indicated in the following chart, the nature of the task determines the program exitto be used.

7. The Coding and Use of Exit Programs7.1

PHASE 1

for

exit rou-

input

for sort

(Phase 1) and

(Phase 3)

input

for

records

records

re-

records

action

intermediate

insuffi-

other

data sets

read

write

labels

a col-

se-

*E15 in Phase 3 for copy only

.XXXXXXXXE11E14E15E16E17E18E61PHASE 2E21E25E27E31E32E15*PHASE 3E35E37E38E39Ehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a61XXXXXXXXXXXXXXXXXXXXXXXXXXProgram Exits and Processing Phases7.2 Programmer'sGuide

Loading the Exit Routines into Main Storage

MODS statement identifies the exits to be taken and indicates the name of the sep-arately compiled, user-written routine to take control at that point.The same routine(e.g., deleting selected records) could take effect in different phases, but cannot be loadedmore than once in a single phase.

that merge and copy are executed entirely in Phase 3 and are therefore restrictedin the exits which they can use.A merge application cannot use exits E11 through E27.

copy application can use exit E15 but not exits E32 or E61.

each routine as a separate program and place it in a partitioned data set or inthe SYSIN input stream; SyncSort copies the SYSIN routines to the SORTMODS libraryfor linkage editing.(If a SYSIN module is to be used at more than one exit pohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aint, eachexit must have its own compiled copy of the module in SYSIN.)If SyncSort linkage editsan exit routine, the module must have an entry point whose name is that of the SyncSortexit; for example, in order to function as an E35 routine, MYEXIT must include an entrypoint or CSECT labeled E35.

a routine has already been link-edited, this can be indicated in the MODS statement.When all the exits in a particular phase need to communicate with one another, theMODS statement can be used to instruct the sort to link-edit them together.

Conventions

following conventions must be observed when using exits.

Exits provided via the MODS control statement will be entered in the addressing

indicated by the linkage editor module attributes.Any exit linkage-edited by

will be entered in 24-bit addressing mode, except a separately linkage-

exit E11, E21, or E31, whhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aich will be entered in the mode set by the compiler

assembler when the module was compiled or assembled.

addresses provided via the 24-bit invoking parameter list format will be entered

the 24-bit address mode.

addresses provided via the 31-bit invoking parameter list will be entered in the

mode indicated in the exit address field.That is, if bit 0 of the exit address

0, the exit is entered in 24-bit mode; if bit 0 of the exit address is 1, the exit is

in 31-bit mode.

exits may return to the sort in either 24- or 31-bit address mode.

an exit was entered in 24-bit address mode, the addresses passed to it will be 24-bit

that have a clean high-order byte containing binary zeros (X'00'). Addresses

to the sort must also be 24-bit values with a high-order byte containing X'00'

though the exithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a could return to the sort in the 31-bit mode.

7. The Coding and Use of Exit Programs7.3

An exit in the 31-bit mode may return an address containing a full 31-bit value.

intending to pass only a 24-bit address must therefore make sure that the ad-

returned has X'00' in the high-order byte.Failure to do so can have unpre-

results.Note that certain addresses within parameter lists are still explicitly

to 24-bit values.For example, E18 exit return parameter lists must consist

fullword entries that are 1-byte codes and 3-byte addresses.

Conventions

standard operating system conventions apply to register usage.Exit routines mustsave and restore Registers 0 and 2-14.The sort/merge places these contents in Register1 and 13-15 for use by the exit routine when it takes control.

1The address of a SyncSohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art parameter list.

The address of a 19-word area.The first 18 words can be used to save

, the 19th word to pass information between Assembler exits.

SyncSort's return address, in the low-order address bits of the register.The

-order bit(s) may have undefined contents.

The address of the entry point of the exit routine, in the low-order address

of the register. The high-order bit(s) may have undefined contents.

Exit Communication Area

an exit routine is given control, Register 13 points to a 19-word area, the first 18of which can be used to save registers.The 19th word of this area can be used to passinformation between Assembler exits.For example, when the COMMAREA PARM isused, the 19th word can be set to point to the exit communication area COMMAREAprovides.The first 2 bytes of this communication area give the length ofhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the area.Theuser is free to change the entire communication area, including the initial halfword.REGISTER 13

↓* Address of communication area↓18-word save area*    ↓0004LIST

://www.wendangwang.comer Communication Area for Assembler Exit Using COMMAREA

.4 Programmer'sGuide

For COBOL or C exits, the address and length of this area are passed in the COBOL or

program's parameter list.In this case, there is no halfword preface - the address pointsdirectly to the communication area.

E11, E21, and E31 - Preparing for Other Exit Routines

exits are unusual in that they are entered only once, at the beginning of their as-sociated phase.Because of this, they may be separately link-edited and are efficientlyused to prepare for other exit routines (e.g., to open files or initialize variables).Thereare no parameter lists or return codes for these exits.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarE32 - Invoked Merge Only: Creating Input Records

exit can only be used for an invoked merge and must be coded in line with the in-voking program.It therefore never appears on the MODS statement.When an E32routine is used, all SORTINnn DD statements will be ignored by the merge; the exit mustsupply all the input records, and the number of input files to be created must be suppliedby either the invoking program's parameter list or the FILES=n parameter on theMERGE control statement.

the merge requires a new input record, SyncSort calls the E32 routine, passingit the address of a two-word parameter list in Register 1.PARAMETER LIST

1: Number of next input file

2: Address of the next input record

.Parameter List for E32

first word of the parameter list contains a hexadecimal representation of the inputfile SyncSort is currently processing.This is http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ainitialized as 0 for the first file and incre-mented by 4 every time a new SORTINnn file is to be accessed.When the E32 encountersend-of-file on a SORTINnn file it should return RC=8 to SyncSort, which will no longerrequest input from that file (i.e., that input file number).

E32 routine must respond to three different cases: (a) SyncSort already has all theinput records; (b) the previous record finished an input file; and (c) there is at least onemore record to be added to the file with this file number.Only in the last case will theE32 supply a record address to the merge, placing it in the second word of the parameterlist.The E32 also places the appropriate return code in Register 15.

7. The Coding and Use of Exit Programs7.5

Return Codes

End of file.This tells SyncSort that a particular file has been completed and

make no further request for records from that file.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aert this record. This tells SyncSort to accept a new record from the input file

.

of merge.This terminates SyncSort with a critical error.1216

.6 Programmer'sGuide

Exits E14, E15, E25, and E35-Deleting, Creating, and ChangingRecords

E14 - Deleting, Summarizing, Changing Records

E14 may be used to change the contents of data fields, or to delete or summarizerecords during Phase 1.Unlike an E15 exit routine, it cannot be used to add records.An E14 exit program requires:

at least one SORTWKnn data set, assigned to disk;fixed length input records.

exit is given control whenever SyncSort is about to add a record to an output se-quence.Since it does not take control before the first record of that sequence, the routinealways has access to a pair of sequenced records (e.g., for summarization purposes).SyncSort passes the exit program a two-worhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad parameter list by loading its address intoRegister 1.The exit must not destroy the contents of this parameter list.The first word,which is on a fullword boundary, contains the address of the record about to be placed inan output sequence; the second word contains the address of the record that has just beenput into the output buffer.PARAMETER LIST

1: Address of record leaving Phase 1

2: Address of the latest record in output buffer

.Parameter List for E14

are two constraints on the type of processing the exit may accord this record pair: Sort control fields should not be changed since this may cause an out-of-sequencecondition.

a record is to be changed, it should first be moved to a work area.

record processing is completed, the exit routine must place the appropriate returncode in Register 15.The exit must save and restore all registers except those ushttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed inlinking to the sort/merge.

Codes

Accept this record. This instructs SyncSort to accept the record whose address

in the first word of the parameter list and place it in the output buffer.The

7. The Coding and Use of Exit Programs7.7

exit must also load the (work area) address of this record into Register 1 before

control to the sort.

Delete this record. This instructs SyncSort to delete the record whose address

in the first word of the parameter list.Do not place the address of this record

Register 1.This return code might be employed, for example, after using

record to update the previous (output) record.Assuming this does not

an output sequence for Phase 1, the next execution of the E14 will

the same address in the second word of the parameter list.

E15 - Creating, Revising ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar Analyzing the Input File

an input data set already exists, this exit is used to add, delete and/or change inputrecords. This exit is also used to analyze SORTIN via HISTOGRM (a HISTE15 applica-tion) or to create the entire input file.It can be used when sorting or copying records.When used in conjunction with an input file, this exit is given control every time a recordis brought into Phase 1 of a sort or Phase 3 of a copy.In passing control to the E15 exitroutine, SyncSort places the address of a parameter list in Register 1.This parameterlist is two words long, aligned on a fullword boundary.In the first word, the first bytecontains X'00'; the last 3 bytes contain the address of the record just brought into Phase

.The first word contains a zero address when there is no such record (i.e., whenSORTIN end-of-file is reached or when the input data set is empty).

2 contains the user address constant.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOn the initial call to the E15 exit, it willcontain the value specified in the invoking parameter list.If this value was specified ina 24-bit invoking parameter list, it will have the high-order byte set to X'00'.If the valuewas omitted or SyncSort was JCL invoked, Word 2 will contain binary zeros.This wordmay be changed by the E15 exit whenever it is entered.If used in a sort application, thevalue will be returned on the subsequent call to the E15. If used in a copy application andan E35 is present, the value on the subsequent call to the E15 will reflect any modificationmade to the User Address Constant by the E35.In a sort application, the initial entryto the E35 will contain the value last returned from the E15.PARAMETER LIST

1: Address of the new record

2: User address constant

.Parameter List for E15

record processing has these two constraints:

If a record is to be chhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aanged, it should first be moved to a work area.

.8 Programmer'sGuide

When the input data set consists of variable length records, the first 4 bytes must

the Record Descriptor Word, giving the length of the record.

the program has finished processing the record, it must place the appropriate re-turn code in Register 15.

the E15 Exit Routine for an Invoked Sort or Copy

SyncSort is initiated from an ATTACH, LINK or XCTL macro, there are two waysto include an E15 exit routine: (1) code the E15 exit routine in line with the invokingprogram and specify the address of its entry point in the appropriate entry of the pa-rameter list; or (2) define the separately compiled routine in the MODS control statement.When the exit routine is coded in line with the calling program, it must supply the entireinput data set; SyncSort will ignore a SORTIN DD statement, if present.Datahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a set cre-ation is done by supplying the sort with one record at a time, placing its address in Reg-ister 1 and a return code of 12 in Register 15.After the last record has been submitted,the exit passes a return code of 8.

Codes

Accept this record.This instructs SyncSort to accept the record the exit has

examined.Place the (work area) address of this record in Register 1.This

code is used when selectively editing records from an input file; it passes

(possibly altered) record back to the sort.The RECORD statement is re-

if the exit routine changes the maximum record length; code the old

length as l1, the new maximum as l2.

this record.SyncSort will delete the record just examined.There is no

to load the address of this record into Register 1.

not return to this exit.This instructs SyncSort to close the exit fohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar the re-

of the sort application.This return code might be used at SORTIN

-of-file (signalled by a zero address in the parameter list) to indicate that

records will not be added at this point.There is no need to load a record

into Register 1 when passing a return code of 8. If SORTIN is present,

current input record and all subsequent records will be processed by

.

a record.This tells SyncSort that the exit routine has located a record

should be added to the input data set before the record whose address

in the parameter list.Load the address of the new record into Register

.When SyncSort returns control to the E15, the parameter list will be un-

.The exit routine can then add another record or process the current

.

return code can be used to add records to the end of http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe input data set

to create the entire input data set.SyncSort returns to the exit routine,

records without changing the parameter list (in these cases, a zero ad-4812

7. The Coding and Use of Exit Programs7.9

dress) until a different return code (i.e., RC=8) is passed.When the input data

is created in this way, the RECORD statement is required and must specify

TYPE and LENGTH.

Terminate SyncSort.This tells SyncSort to terminate and return to the calling

or the supervisor.SyncSort uses a completion code of 16 to indicate

the sort was unsuccessful.

a COBOL E15 Exit Routine

COBOL E15 exit program can be indicated through the EXEC statement's PARM op-tion (PARM='E15=COB'), the MODS control statement or the $ORTPARM DD statement.An E15 exit cannot be coded in COBOL when running Tape Sort.

any othttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aher E15 exit routine, the COBOL E15 exit routine is called each time a recordis brought into Phase 1 of a sort or Phase 3 of a http://www.wendangwang.communication between SyncSortand the COBOL exit takes place in the LINKAGE SECTION of the COBOL program.For example, records are passed to the COBOL routine in the second definition(RECORD-UP) area of the LINKAGE SECTION.

the COBOL exit routine uses any verb (EXHIBIT, DISPLAY, TRACE) which results inoutput to the SYSOUT DD statement, there is a potential conflict with SyncSort's use ofthis DD statement. It is therefore recommended that the user separate the output byusing either SyncSort's MSGDD PARM option or the COBOL compiler's SYSx parm.If the COBOL E15 exit routine is written in OS/VS COBOL and uses OS/VS COBOL li-braries or no libraries, specify the COBEXIT=COB1 PARM option.If the COBOL E15exit routine is written in OS/VS COBOL or in VS COBOL II or COBOL/370 and uses http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aVSCOBOL II or COBOL/370 libraries, specify the COBEXIT=COB2 PARM option.VSCOBOL II and COBOL/370 run-time library modules typically require more main storagethan OS/VS COBOL library modules.The amount of additional storage depends on VSCOBOL II of COBOL/370 installation options. When VS COBOL II or COBOL/370 run-time library modules are used, it may be necessary to account for this additional storageby adjusting the b value of the Exit-Name parameter on the MODS statement.

LINKAGE SECTION

LINKAGE SECTION examples that follow show the parameters required for passingfixed length and variable length records to the sort.The data-names and conditionalnames used in the examples are arbitrary but each definition is required.The completeprograms from which the examples are taken follow the discussion of the exit.

.10 Programmer'sGuide

Example 1: Fixed Length RecordsLINKAGE SECTION.

EXIT-STATUhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aS

FIRST-TIME

MOST-TIME

LAST-TIME

RECORD-UP.

FILLER

R-SEQ2

FILLER

WORK

DUMMY1

DUMMY2

DUMMY3

DUMMY4

DUMMY5

COMM-LEN

COMMUNICATION-AREA.

COMM-AREA OCCURS 1 TO 256 TIMES

ON COMM-LEN PIC X.PIC 9 (8) COMPUTATIONAL.VALUE00.VALUE04.VALUE08.PICPICPICPICPICPICPICPICPIC9(6).9(2).X(92).X(100).X.X.X.X.X.PIC9(4) COMPUTATIONAL.

For the first definition (EXIT-STATUS) specify PIC 9(8) COMPUTATIONAL. (This

defines exit status codes.)When using 88 levels to define the exit status codes,specify values 00, 04, and 08.

the second definition (RECORD-UP) define the SORTIN record.

the third definition (WORK) define the record that will be passed to SyncSort.(This is the &quot;work area.&quot;)

the fourth through the eighth definitions dehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1afine dummy areas.

the ninth definition (COMM-LEN) specify PIC 9(4) COMPUTATIONAL.Thisarea defines the communication area length.

the tenth definition (COMMUNICATION-AREA) code an OCCURS clause DE-PENDING ON data-name PIC X.

7. The Coding and Use of Exit Programs7.11

Example 2:Variable Length RecordsLINKAGE SECTION.

EXIT-STATUSPIC 9 (8) COMPUTATIONAL.

FIRST-TIMEVALUE00.

MOST-TIMEVALUE04.

LAST-TIMEVALUE08.

RECORD-UP.

RUOCCURS 1 TO 100 TIMES

ON LEN-RUPIC X.

WORK.

WKOCCURS 1 TO 100 TIMES

ON LEN-WKPIC X.

IN-BUFPICX(100).

DUMMYPICX(4).

LEN-RUPIC9(8)COMPUTATIONAL.

LEN-WKPIC9(8)COMPUTATIONAL.

LEN-IBPIC9(8)COMPUTATIONAL.

COMM-LENPIC9(4)COMPUTATIONAL.

COMMUNICATION-AREA.

COMM-AREA OCCURS 1 TO 256 TIMES

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarDEPENDING ON COMM-LEN PIC X.

For the first definition (EXIT-STATUS) specify PIC 9(8) COMPUTATIONAL. (Thisarea defines exit status codes.)

the second definition (RECORD-UP) code an OCCURS clause with the DE-PENDING ON data-name option specifying (1) The minimum and maximum numberof bytes the variable SORTIN records contain (do not include 4 bytes for the RDW)and (2) DEPENDING ON data-name PIC X.Data-name is defined in the sixth defi-nition in the LINKAGE SECTION.

the third definition (WORK) code an OCCURS clause with the DEPENDING ONdata-name option specifying (1) The minimum and maximum number of bytes forvariable length records to be passed to SyncSort (do not include 4 bytes for the RDW)and (2) DEPENDING ON data-name PIC X.Data-name is defined as the seventhdefinition in the LINKAGE SECTION.

the fourth definition specify a dummy level 01 data-name of any number of bytes.(IN-BUF is the dahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ata-name used in this example.)Note that the level 01 data-name,used here as a dummy address, has no effect on the E15 routine for variable lengthrecords.The address is usually used as a buffer pointer in the COBOL E35 exitroutine.By using it in the E15 LINKAGE SECTION, SyncSort is able to use thesame parameter list for both COBOL exits E15 and E35.

the fifth definition specify a dummy area.

.12 Programmer'sGuide

For the sixth definition (LEN-RU) specify data-name PIC 9(8) COMPUTATIONAL.

is where SyncSort passes the length of the SORTIN record to the COBOL exit.For the seventh definition (LEN-WK) specify data-name PIC 9(8) COMPUTA-TIONAL.This is where the E15 routine passes the length of the work area recordto SyncSort.

the eighth definition define a dummy area.

the ninth definition (COMM-LEN) specify PIC 9(4) COMPUTATIONAL.Thisarea defines the communication area lenhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1agth.

the tenth definition (COMMUNICATION-AREA) code an OCCURS clause DE-PENDING ON data-name PIC X.

IDENTIFICATION, ENVIRONMENT, and DATA Divisions

always, the COBOL program must contain the entries required by the compiler forthese program divisions.Code the optional entries in these divisions according to therequirements of the application.

WORKING-STORAGE SECTION

the exit routine inserts records into the final merge and replaces records passed fromSyncSort, the insertion record and the replacement record may be defined in this section.These records will be moved to the WORK area described in the LINKAGE SECTION,so be sure that the PICTURE clause or the OCCURS clause in the WORK area is correctfor these records.

section may also define the return codes as 77-level data items.Alternatively, thesecodes can be specified as literals in the MOVE instruction.(MOVE lithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeral toRETURN-CODE.)Note that RETURN-CODE is the name of a predefined storage areain COBOL used to pass return codes to the sort; RETURN-CODE should not be definedin the exit routine.

PROCEDURE DIVISION

the USING option on the PROCEDURE DIVISION header.Each identifierspecified after USING must be the same as those described in the 01-level of the LINK-AGE SECTION.Taking for example the identifiers defined in the fixed length recordLINKAGE SECTION shown here, they would appear as: PROCEDURE DIVISION US-ING EXIT-STATUS, RECORD-UP, WORK, DUMMY1, DUMMY2, DUMMY3, DUMMY4,DUMMY5, COMM-LEN, COMMUNICATION-AREA.

GOBACK statement is used to return control to SyncSort.Do not use the EXITstatement as it will cause unpredictable results.Be sure that SyncSort receives a validreturn code before the GOBACK statement is executed.

7. The Coding and Use of Exit Programs7.13

EXIT-STATUS Codeshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a (Fixed and Variable Length Records)

First record.SyncSort uses this Code to indicate the first call to the COBOL

and that the first record from SORTIN is in the RECORD-UP area.

records.This is used for all calls except the first one when there are re-cords in the RECORD-UP area.After Code 00 has been issued, Code 04 ispassed to the exit until there is no record for the sort to pass to theRECORD-UP area.

records passed.This indicates that the last SORTIN record has alreadybeen processed by the exit.Do not attempt to reference the record again.Nomore records will be passed to the exit routine.Note that if the SORTIN dataset is empty, 08 will be passed every time including the first time.0408

-CODE Codes (Fixed and Variable Length Records)

Accept this record.This instructs SyncSort to accept the (unaltered) record in

RECORD-UP area.

this record.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSyncSort will delete the current record in the RECORD-UParea.

not return to this exit.This instructs SyncSort to close the exit for the re-mainder of the sort application.This return code might be used at SORTINend-of-file (Exit Status Code 08) to indicate that extra records will not be addedat this point. If SORTIN is present, the current input record and all subse-quent records will be processed by SyncSort.

a record.This instructs SyncSort to add the record in the WORK areato the input data set just ahead of the current record in the RECORD-UP area.When SyncSort returns control to the E15, the same record will be in theRECORD-UP area.The exit routine can then add another record from theWORK area or process the current record in RECORD-UP.

SyncSort.SyncSort will end its program and return to the callingprogram or the Supervisor. SyncSort will issue a completion code of 16 to in-dicate thathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the sort was unsuccessful.

current record.SyncSort will replace the current record in theRECORD-UP area with the record in the WORK area.Be sure that the recordin the WORK area is valid before passing it to SyncSort.48121620

Change a Record

order to change the record in the RECORD-UP area, first move it to the WORK area.All changes are made to the WORK area copy, which replaces the record in RECORD-UPwhen 20 is moved to RETURN-CODE.

.14 Programmer'sGuide

Sample COBOL E15, Fixed Length RecordsIDENTIFICATION DIVISION.

-ID. E15FL13C.

DIVISION.

SECTION.

-COMPUTER. IBM-370.

-COMPUTER. IBM-370.

-OUTPUT SECTION.

-CONTROL.

-O-CONTROL.

DIVISION.

SECTION.

-STORAGE SECTION.

EVEN-FLAG

USER-RETURN-CODE88ACCEPhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aT-REC88DELETE-REC88END-EXIT88INSERT-REC88END-SORT88REPL-RECCHANGE-REC.

C-REC

C-INCR

C-BLANK

-REC.

I-REC

I-INCR

I-BLANK

.

BLANKS

TITL

COUNTERPICPIC0.4.8.12.16.20.9(2) VALUE ZERO.9(8)COMPUTATIONAL.VALUEVALUEVALUEVALUEVALUEVALUEPICPICPICX(6) VALUE 'CHANGE'.9(4) VALUE ZERO.X(90) VALUE ZERO.01 PICX(6) VALUE 'INSERT'.PIC9(4) VALUE ZERO.PIC X(90) VALUE SPACES.01  PIC X(10) VALUE ' E15'.PIC X(25) VALUE 'TOTAL RECORDS OUT'.PIC9(8)VALUE0.

7. The Coding and Use of Exit Programs7.15

Sample COBOL E15, Fixed Length Records (Continued)LINKAGE SECTION.

EXIT-STATUS

FIRST-TIME

LAST-TIME

RECORD-UP.07FILLER07R-SEQ107FILLERWORKPIC9(8)COMPUTATIONAL.VALUE00.VALUE08.PIC9(6).PIC9(2).PICX(92).PICX(100).

DIVISION USING EXIT-STATUS, RECORD-UP,WORK.

Chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOUNTER GREATER THAN 100

0 TO RETURN-CODE

TO RETURN-TO-SORT.

LAST-TIME GO TO RETURN-TO-SORT.

-SEQ1EQUAL0

4 TO RETURN-CODE

TO RETURN-TO-SORT.

-SEQ1EQUAL5

12 TO RETURN-CODE

INSRT-REC TO WORK

TO RETURN-TO-SORT.

-SEQ1EQUAL6

20 TO RETURN-CODE

CHANGE-REC TO WORK

TO RETURN-TO-SORT.

0 TO RETURN-CODE.

-TO-SORT.

1 TO COUNTER.

LAST-TIME MOVE 8 TO RETURN-CODE

.

.

.16 Programmer'sGuide

Sample COBOL E15, Variable Length RecordsIDENTIFICATION DIVISION.

-ID. E15VL19C.

DIVISION.

SECTION.

-COMPUTER. IBM-370.

-COMPUTER. IBM-370.

-OUTPUT SECTION.

-CONTROL.

-O-CONTROL.

DIVISION.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a SECTION.

-STORAGE SECTION.

EVEN-FLAG

-RETURN-CODE88ACCEPT-REC88DELETE-REC88END-EXIT88INSERT-REC88END-SORT88REPL-RECPIC 9(2) VALUE ZERO.PIC 9(8) COMPUTATIONAL.0.4.8.12.16.20.VALUE VALUE VALUE VALUEVALUEVALUE

CHANGE-REC.

C-REC

C-INCR

C-BLANK

INSRT-REC.

I-REC

I-INCR

I-BLANK

TOTAL.

BLANKS PICPICX(6)VALUE'CHANGE'.PIC9(4)VALUEZERO.PIC X(90) VALUE SPACES.PIC X(6) VALUE 'INSERT'.PIC 9(4) VALUE ZERO.PIC X(90) VALUE SPACES.X(10) VALUE ' E15'.

7. The Coding and Use of Exit Programs7.17

Sample COBOL E15, Variable Length Records (Continued)05TITL PIC

COUNTER PIC

SECTION.

EXIT-STATUS

FIRST-TIME

MOST-TIME

LAST-TIMEX(25)VALUE'TOTALRECORDSOUT'.9(8) VALUE 0.PIC 9(8)COMPUTATIONAL.VALUE00.VALUE04.VALUE08.

REhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCORD-UP.

RU OCCURS1TO100TIMES

ON LEN-RUPIC X.

WORK.

WK OCCURS1TO100TIMES

ON LEN-WKPIC X.

IN-BUFPICX(100).

DUMMYPIC 9(8) COMPUTATIONAL.

LEN-RUPIC 9(8) COMP.

LEN-WKPIC 9(8) COMP.

DIVISION USING EXIT-STATUS, RECORD-UP, WORK,

-BUF, DUMMY, LEN-RU, LEN-WK.

NOT FIRST-TIME

1 TO COUNTER

0 TO RETURN-CODE.

COUNTER LESS THAN 50

54 TO LEN-WK

1 TO I-INCR

INSRT-REC TO WORK

12 TO RETURN-CODE

TO RETURN-TO-SORT.

COUNTER LESS THAN 75

44 TO LEN-WK

1 TO C-INCR

CHANGE-REC TO WORK

.18 Programmer'sGuide

Sample COBOL E15, Variable Length Records (Continued)MOVE 20 TO RETURN-CODE

TO RETURN-TO-SORT.

COUNTER LESS THAN 100

80 TO LEN-WK

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aD 1 TO I-INCR

12 TO RETURN-CODE

INSRT-REC TO WORK.

TO RETURN-TO-SORT.

COUNTER LESS THAN 200

4 TO RETURN-CODE

TO RETURN-TO-SORT.

-TO-SORT.

LAST-TIME MOVE 8 TO RETURN-CODE

.

.

a C E15 Exit Routine

C E15 exit program is indicated by the MODS control statement. An E15 exit cannotbe coded in C when running Tape Sort.

any other E15 exit routine, the C E15 exit routine is called each time a record isbrought into Phase 1 of a sort or Phase 3 of a copy.SyncSort and the C exit communicatethrough arguments defined in the function header.For example, records are passed tothe C routine by the address presented in the second argument in the function parameterlist.No storage is reserved in the exit program because the records exist elsewhere.The C E15 exit routine can be written using either thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe C370 V2R1 compiler with theV2R2 C370 Library, the SAA AD/Cycle C370 V1R2 Compiler and Library or the C/C  for MVS/ESA V3R1.1 or higher Compiler and Library.When using the LE/370 run timelibrary modules, it may be necessary to account for this additional storage by adjustingthe b value of the Exit-Name parameter on the MODS statement.

Communication

parameter list structure required for passing fixed length and variable length recordsbetween the sort and the exit is detailed in the following section. The parameter namesused in the examples are arbitrary but each definition is required. Complete sample pro-grams showing the use of the argument lists are presented following the discussion of theexit interface.

7. The Coding and Use of Exit Programs7.19

Fixed Length Records - Function Definitionint E15exit (int* exit_status,

_ru*record_up,

_ins_rep*work,

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aint* dummy1, int* dummy2, int* dummy3,

* dummy4, int* dummy5,

*comm_len,

_ca*communication_area)

following describes the parameters used in the preceding definition.

_statusThis parameter points to a variable containing one of the fol-

exit status codes:

First record.SyncSort uses this code to indicate

first call to the C exit and that the first record

SORTIN is in the record_up area.If the

is empty or does not exist, a 08 status will

passed the first time.

records.This is used for all calls except the

one when there are records in the record_up

. After Code 00 has been issued, Code 04 is

to the exit until there is no record for the

to pass to the record_up area.

records passed.This indicates that the last

record has alreadhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay been processed by the

. Do not attempt to reference the record again.

more records will be passed to the exit routine.

that if the SORTIN data set is empty or does

exist, 08 will be passed every time including the

time.0408

_upThe record_up parameter contains a pointer to the record be-

passed to the E15 from the SORTIN. The struct_ru data

represents a structure that describes the fields within the

record.

work parameter contains a pointer to a work area that is

be used to hold an inserted or replaced record returned from

E15. The struct_ins_rep data type represents a structure

describes the fields within the inserted or replaced re-

.work

.20 Programmer'sGuide

dummy1 - dummy5Theseparametersdefineunusedplaceholders.Theyareused

variable lengthhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a E15 and E35 communication. Their defi-

here allows a common parameter list for fixed length

variable length C E15 and E35 exits.

parameter points to a variable that defines the commu-

area length.

communication_area parameter contains a pointer to the

area. The struct_ca data type represents a

that describes the fields in the communication http://www.wendangwang.comm_lencommunication_area

Length Records - Function Definitionint E15exit (int* exit_status,

*record_up,

*work,

* dummy1, int* dummy2,

*len_ru,

*len_wk,

*dummy3,

*comm_len,

_ca*communication_area)

following describes the parameters used in the preceding definition.

_statusThis parameter points to a variable containing exit status

.See the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aexit_status definition for a fixed length C E15

for the code definitions.

record_up parameter contains a &quot;universal&quot; pointer to the

being passed to the E15 from the SORTIN.The void*

can be cast to point an appropriate structure to de-

the record passed to the exit.This allows different re-

structures, as is common with variable length records, to

a single pointer definition.

work parameter contains a &quot;universal&quot; pointer to a work

that is to be used to hold an inserted or replaced record

from the E15.The void* pointer can be cast to point

appropriate structure to describe the work record.

.Theyareused

C E35 communication.Their definition here allows a

parameter list for C E15 and E35 exits.record_upworkduhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ammy1 - dummy3

7. The Coding and Use of Exit Programs7.21

len_ruThis parameter points to a variable that defines the length of

SORTIN record passed to the E15.This is the length of

record referred to in the record_up parameter.

parameter points to a variable that defines the length of

record to be inserted or used as a replacement for the

_up record.This is the length of the record referred to

the work parameter.This field must be set by the exit

an insert or replace operation is performed.

parameter points to a variable that defines the commu-

area length.

communication_area parameter contains a pointer to the

area. The struct_ca data type represents a

that describes the fields in the communication area.len_wkcomm_lencommunication_area

-CODEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Codes (Fixed and Variable Length Records)

RETURN statement is used to return control to SyncSort. It must indicate one of thefollowing return values to indicate the action to be taken by SyncSort.

Accept this record.This instructs SyncSort to accept the (unaltered) record in

record_up area.

this record.SyncSort will delete the current record in the record_up

.

not return to this exit.This instructs SyncSort to close the exit for the re-

of thesort application. This return code might beusedat SORTIN

-of-file (exit_status code 08) to indicate that extra records will not be added

this point.If SORTIN is present, the current input record and all subse-

records will be processed by SyncSort.

a record.This instructs SyncSort to add the record in the work area to

input data set just ahead of the currenhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at record in the record_up area. When

returns control to the E15, the same record will bein the record_up

. The exit routine can then add another record from the work area or

the current record in record_up. When inserting a variable length re-

, insure that its length is indicated in the len_wk parameter.

SyncSort. SyncSort will end its program and return to the calling

or the Supervisor. SyncSort will issue a completion code of 16 to in-

that the sort was unsuccessful.

current record.SyncSort will replace the current record in the

_up area with the record in the work area.Be sure that the record in

work area is valid before passing it to SyncSort.When replacing a variable

record, insure that its length is indicated in the len_wk parameter.48121620

.22 Programmer'sGuide

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparHow to Change a Record

change the record in the record_up area, first move it to the work area.All changesare made to the work area copy, which replaces the record in record_up when the returnvalue from the exit is 20.

C E15, Fixed Length Records#define FIRST_TIME0

#define MOST_TIME 4

#define LAST_TIME 8

#define ACCEPT_REC0

#define DELETE_REC4

#define END_EXIT8

#define INSERT_REC12

#define END_SORT16

#define REPL_REC20

_Packed struct record

[6];

[4];

_no;

t_ru;

#include &lt;stdio.h&gt;

#include &lt;stdlib.h&gt;

#include &lt;string.h&gt;

SMPE15FB(int* exit_status,t_ru* record_up,t_ru* work,int* dummy1,

* dummy2,int* dummy3,int* dummy4,int* dummy5,int* comm_len,

*communication_area)

counter=0;

ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acode,return_code;

* text1=&quot;CHANGE&quot;;

* text2=&quot;INSERT&quot;;

(counter &gt; 10) return_code=ACCEPT_REC;

_to_sort;

(*exit_status == LAST_TIME) return_code=END_EXIT;

_to_sort;

7. The Coding and Use of Exit Programs7.23

Sample C E15, Fixed Length Records (Continued)sscanf(record_up-&gt;code,&quot;M&quot;,&amp;icode);

(icode==0)  return_code=DELETE_REC;

_to_sort;

(icode==5)

(work-&gt;name,text2,6);

(work-&gt;code,&quot;M&quot;,icode counter 8);

-&gt;serial_no=300;

_code=INSERT_REC;

_to_sort;

(icode==6)

(work-&gt;name,text1,6);

(work-&gt;code,&quot;M&quot;,icode 1);

-&gt;serial_no=record_up-&gt;serial_no 200;

_code=REPL_REC;

_to_sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at;

_code=ACCEPT_REC;

_to_sort:

;

(*exit_status==LAST_TIME)

return_code=END_EXIT;

(&quot;E15 total number of records handled:%d&quot;,counter);

(return_code);

.24 Programmer'sGuide

Sample C E15, Variable Length Records#define FIRST_TIME0

#define MOST_TIME 4

#define LAST_TIME 8

#define ACCEPT_REC0

#define DELETE_REC4

#define END_EXIT8

#define INSERT_REC12

#define END_SORT16

#define REPL_REC20

#define MAX_RLEN104

_Packed struct record1

[6];

;

[MAX_RLEN-14];

t_ru1;

_Packed struct record2

[10];

;

t_ru2;

#include &lt;stdio.h&gt;

#include &lt;stdlib.h&gt;

#include &lt;strings.h&gt;

SMPE15VB(int* exihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at_status,void* record_up,void* work,int* dummy1,

* dummy2,int* len_ru,int* len_wk,int* dummy3,int* comm_len,

*communication_area)

counter=0,i_incr=0,i_number=0;

return_code;

*text1=&quot;CHANGE E15&quot;;

*text2=&quot;INSERT E15&quot;;

_ru1 * p_record1,*pwork1;

_ru2 * p_record2,*pwork2;

_record1 = (t_ru1 *)record_up;

= (t_ru1 *)work;

_record2 = (t_ru2 *)record_up;

= (t_ru2 *)work;

(*exit_status != FIRST_TIME) counter  ;

_code=ACCEPT_REC;

7. The Coding and Use of Exit Programs7.25

Sample C E15, Variable Length Records (Continued)if (counter&lt;50)

(*len_ru == 14)

*len_wk = 14;

_number  ;

-&gt;number=i_number;

(pwork2-&gt;title,text2,10);

*len_wk = 54;

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ari_incr  ;

-&gt;incr=i_incr;

(pwork1-&gt;rec,text2,6);

_code=INSERT_REC;

_to_sort;

(counter&lt;75)

(*len_ru == 14)

*len_wk = 14;

-&gt;number=p_record2-&gt;number 1;

(pwork2-&gt;title,text1,10);

*len_wk = 54;

-&gt;incr=p_record1-&gt;incr 1;

(pwork1-&gt;rec,text1,6);

_code=REPL_REC;

_to_sort;

(counter&lt;100)

(*len_ru == 14)

*len_wk = 14;

_number  ;

-&gt;number=i_number;

(pwork2-&gt;title,text2,10);

.26 Programmer'sGuide

Sample C E15, Variable Length Records (Continued) else

*len_wk = 80;

_incr  ;

-&gt;incr=i_incr;

(pwork1-&gt;rec,text2,6);

_code=INhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSERT_REC;

_to_sort;

(counter&lt;200)

_code=DELETE_REC;

_to_sort;

_to_sort:

(*exit_status==LAST_TIME)

return_code=END_EXIT;

(&quot;E15 total number of records handled:%d&quot;,counter);

(return_code);

E25 - Deleting, Changing, Summarizing Records

gives control to exit E25 each time it is about to place a record in a Phase 2output sequence, except for the first record of that sequence.Because all or part of theinput data set may skip this phase, it may be necessary to include an E35 to do the jobof the E25 during Phase 3.If it is possible to use the SUM control statement in place ofthe exit, this is recommended.

constraints apply to the coding of an E25 exit routine:

The exit may not add records.The exit may not change sort control fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aields.The exit may not destroy the contents of the parameter list.

will place the address of a 2-word parameter list in Register 1 each time itpasses control to the E25 routine.The first word, which is on a fullword boundary, willcontain the address of the record about to leave Phase 2.The second word will containthe address of the record that has already passed into the output area.Note that the firstbyte of each word contains zeros.

7. The Coding and Use of Exit Programs7.27

PARAMETER LIST

1:Address of record leaving Phase 2

2:Address of record already in output area

.Parameter List for E25

order to change the record leaving Phase 2, the E25 exit program must first move itto a work area.(The record in the output area may be changed, but must be left whereit is.)To sum two records, place the sum in the output area record and delete the recordhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aleaving Phase 2.

the record pair has been processed by the E25, a return code is placed into Register15 and control returns to SyncSort.

Codes

Accept this record.To instruct SyncSort to accept the record leaving Phase 2,

changed or unchanged, place return code 0 into Register 15.The

(work area) address of the record to be accepted must be placed into Register

.

this record.This tells SyncSort to delete the record about to leave Phase

.It is not necessary to place the address of this record in Register 1.The next

SyncSort returns control to the exit program, the address of a new record

be in word 1 of the parameter list but word 2 will be unchanged.(This

further summarization, for example.)

SyncSort.SyncSort will end its program and return to the calling

or the supervisor.SyncShttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aort will give the user a completion code of

to indicate that the sort was unsuccessful.416

E35 - Adding, Deleting and Changing Records

an output data set is available, the user may elect to incorporate this exit to add,delete or change records at the end of Phase 3.In the absence of an output data set, thisexit has full responsibility for output processing and, under normal conditions, will deleteevery record passed by the sort.

record processing has these constraints:

If a record is to be changed, it should first be moved to a work area.The exit program may not destroy the contents of the parameter list.A user exit may not take checkpoints.

.28 Programmer'sGuide

Coding the E35 Exit Routine for an Invoked Sort/Merge/Copy

SyncSort is initiated from an ATTACH, LINK or XCTL macro, there are two waysto include an E35 exit routine: (1) cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ade the E35 exit routine in line with the invokingprogram and specify the address of its entry point in the appropriate entry of the callingprogram's parameter list; or (2) define the separately compiled routine in the MODScontrol statement.When the exit routine is coded in line with the invoking program, itmust handle all output processing; SyncSort will ignore a SORTOUT DD statement andan OUTFIL control statement, if present.

E35 Parameter List

exit routine is given control each time SyncSort is about to place a record in theoutput area after the final merge.In passing control to the E35 exit routine, SyncSortplaces the address of a parameter list in Register 1.The parameter list starts at afullword boundary and is 3 words long; the first byte of each word contains binary zeros.The first word contains the address of the record about to leave Phase 3; after the lastrecord has been passed, this word will contahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ain zeros.The second word contains the ad-dress of the record already in the output area; when the first record is passed, this wordwill contain zeros.

third word contains the user address constant. It contains either the last value setin it by an E15 exit routine or, if not modified by an E15 exit routine, the initial valuefrom the user exit address constant provided in the invoking parameter list.If the valuewas obtained from the 24-bit invoking parameter list, it is limited to 24 bits with thehigh-order byte set to X'00'.

the user exit address constant was not provided or if SyncSort was JCL-invoked, it willcontain binary zeros.This word may be changed by the E35 exit routine whenever it isentered, and it will remain the same on all subsequent entries to the E35 exit routine.PARAMETER LIST

1:Address of record leaving Phase 3

2:Address of record in output area

3:User addresshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a constant.

.Parameter List for E35

Codes

Accept this record.This instructs SyncSort to accept the record now leaving

3.Place the (work area) address of this record in Register 1.This re-turn code is used when selectively editing records for output; it passes the

7. The Coding and Use of Exit Programs7.29

(possibly altered) record back to the sort.The RECORD statement is required

this exit routine changes the maximum record length.

Delete this record.SyncSort will delete the record leaving Phase 3.There is

need to load the address of this record into Register 1.When SyncSort re-

control to the E35, the first word of the parameter list (the address of the

leaving Phase 3) will refer to a new record, but the second word (the

of the output area record) will be unchanged.

E35.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a This instructs SyncSort to process any remaining records

showing them to the E35 exit. Register 1 is ignored for processing this

code.When this return code is used at end-of file (signalled by a zero

in the first word of the parameter list), it indicates that E35 is also

and will not add additional records. When used before end-of-file, it

that SyncSort should process the &quot;current&quot; record passed to the E35,

any subsequent records, as if there were no E35 present. Note that when

is not creating any output files (SORTOUT or SORTOFxx) and E35

the only &quot;output&quot;, SyncSort terminates immediately, since any subsequent

will never be seen.Note that if an XSUM data set was being created,

will only contain records generated prior to the return code of 8.

a record.This telhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1als SyncSort to add a record just before the record is

to leave Phase 3.Load the address of the inserted record into Register

.When SyncSort returns control to the E35 exit routine, the first word of the

list (the address of the record leaving Phase 3) will be unchanged,

the second word (the address of the output area record) will refer to the

record.The exit routine can then add another record or process the

one.

SyncSort.This tells SyncSort to end its program and return to the

program or the supervisor.SyncSort uses a completion code of 16 to

that the sort was unsuccessful.81216

a COBOL E35 Exit Routine

COBOL E35 exit program can be indicated through the EXEC statement PARM option(PARM='E35=COB'), the MODS control statement or the $ORTPARM DD statement.An E35 exit cannot be coded inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a COBOL when running Tape Sort.

any other E35 exit routine, the COBOL E35 is called each time a record is broughtout of Phase http://www.wendangwang.communication between SyncSort and the COBOL exit takes place in theLINKAGE SECTION of the COBOL program.For example, records are passed to theCOBOL routine in the second definition (RECORD-UP) area of the LINKAGE SECTION.No storage is reserved in the exit program because the records exist elsewhere.

the COBOL exit routine uses any verb (EXHIBIT, DISPLAY, TRACE) which results inoutput to the SYSOUT DD statement, there is a potential conflict with SyncSort's use of

.30 Programmer'sGuide

this DD statement.It is therefore recommended that the user separate the output byusing either SyncSort's MSGDD PARM option or the COBOL compiler's SYSx parm.If the COBOL E35 exit routine is written in OS/VS COBOL and uses OS/VS COBOL li-braries or no libraries, spechttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aify the COBEXIT=COB1 PARM option. If the COBOL E35 exitroutine is written in OS/VS COBOL or in VS COBOL II or COBOL/370 and uses VSCOBOL II or COBOL/370 libraries, specify the COBEXIT=COB2 PARM option.VSCOBOL II or COBOL/370 run-time library modules typically require more main storagethan OS/VS COBOL library modules.The amount of additional storage depends on VSCOBOL II or COBOL/370 installation options.When VS COBOL II or COBOL/370 run-time library modules are used, it may be necessary to account for this additional storageby adjusting the b value of the Exit-Name parameter on the MODS statement.

LINKAGE SECTION

LINKAGE SECTION examples that follow show the parameters required for passingfixed length and variable length records to the sort.The data-names and conditionalnames used in the examples are arbitrary but each definition is required.The completeprograms from which the examples are taken follow the dishttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acussion of the exit.

1: Fixed Length Records

7. The Coding and Use of Exit Programs7.31

LINKAGE SECTION.

EXIT-STATUS

FIRST-TIME

MOST-TIME

LAST-TIME

RECORD-UP.05RUWORK.05WKIN-BUF.05IBDUMMY1DUMMY2DUMMY3DUMMY4COMM-LENCOMMUNICATION-AREA.

PIC9(8)COMPUTATIONAL.VALUE00.VALUE04.VALUE08.PICX(100).PICX(100).PICPICPICPICPICX(100).X(4)http://www.wendangwang.comPUTATIONAL.PIC9(4)COMM-AREA OCCURS 1 TO 256 TIMES

ON COMM-LEN PIC X.

PICTURE and VALUE clauses for (1) the record passed from SyncSort, (2) the recordWORK area, and (3) the record in the output buffer are application-specific.

For the first definition (EXIT-STATUS) specify PIC 9(8) COMPUTATIONAL.When

88 levels to define exit status codes, sphttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aecify values 00, 04, and 08.

the second definition (RECORD-UP) define the record leaving Phase 3.

the third definition (WORK) define the record that SyncSort is to put in theoutput data set.This is the &quot;work&quot; area.

the fourth definition (IN-BUF) define the record in the output data set.

the fifth definition define a dummy area with PIC X(4).

the sixth through the eighth definition define dummy areas.

the ninth definition (COMM-LEN) specify PIC 9(4) COMPUTATIONAL.Thisarea defines the communication area length.

.32 Programmer'sGuide

the tenth definition (COMMUNICATION-AREA) code an OCCURS clause DE-PENDING ON data-name PIC X.

2:Variable Length Records

SECTION.01 EXIT-STATUS 88FIRST-TIME 88MOST-TIME 88LAST-TIME01

-UP.

RU

(8)COMPUTATIONAL.

.Vhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aALUE04.VALUE08.

1 TO 100 TIMESDEPENDING ON LEN-RU

X.

.05WKIN-BUF.05IB

1 TO 100 TIMESDEPENDING ON LEN-WKOCCURS 1 TO 100 TIMESDEPENDING ON LEN-IBPICPICPICPICPIC

(4)9(8)9(8)9(8)9(4)

X.

X.

01 01 01 01 01

-RULEN-WKLEN-IBCOMM-LEN

://www.wendangwang.comPUTATIONAL.

-AREA.

COMM-AREA OCCURS 1 TO 256 TIMES

ON COMM-LEN PIC X.

the first definition (EXIT-STATUS) specify PIC 9(8) COMPUTATIONAL. Whenusing 88 levels to define exit status codes, specify values 00, 04, and 08.

the second definition (RECORD-UP) code an OCCURS clause with the DE-PENDING ON data-name option specifying (1) the minimum and maximum numberof bytes of your variable length records leaving Phase 3 (do not include 4 bytes for theRDW) and (2) DEPENDING ON data-name PIC http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aX.Data-name is defined in the sixthdefinition in the LINKAGE SECTION.

the third definition (WORK) code an OCCURS clause with the DEPENDING ONdata-name option specifying (1) the minimum and maximum number of bytes forvariable length records you will pass to SyncSort (do not include 4 bytes for the RDW)

7. The Coding and Use of Exit Programs7.33

and (2) DEPENDING ON data-name PIC X.Data-name is defined as the seventhdefinition in the LINKAGE SECTION.This area is used for the &quot;work&quot; area.

the fourth definition (IN-BUF) define records in the output area.Code an OC-CURS clause with the DEPENDING ON data-name option specifying (1) the mini-mum and maximum number of bytes for variable length records in the output dataset (do not include 4-bytes for the RDW) and (2) DEPENDING ON data-name PICX.Data-name is defined as the eighth definition in the LINKAGE SECTION.For http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe fifth definition define a dummy area with PIC X(4).

the sixth definition (LEN-RU) specify PIC 9(8) COMPUTATIONAL.SyncSortwill pass the length of the record leaving Phase 3 in this area.

the seventh definition (LEN-WK) specify PIC 9(8) COMPUTATIONAL.The E35routine passes SyncSort the length of the record in the work area in this section.For the eighth definition (LEN-IB) specify PIC 9(8) COMPUTATIONAL.SyncSortpasses the length of the record in the output area in this section.

the ninth definition (COMM-LEN) specify PIC 9(4) COMPUTATIONAL.Thisarea defines the communication area length.

the tenth definition (COMMUNICATION-AREA) code an OCCURS clause DE-PENDING ON data-name PIC X.

IDENTIFICATION, ENVIRONMENT, and DATA Divisions

always, the COBOL program must contain the entries required by the compiler forthese program divhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aisions.Code the optional entries in these divisions according to therequirements of the application.

WORKING-STORAGE SECTION

the exit routine inserts records into the final merge and replaces records passed fromSyncSort, the insertion record and the replacement record may be defined in this section.These records will be moved to the WORK area described in the LINKAGE SECTION,so be sure that the PICTURE clause or the OCCURS clause in the WORK area is correctfor these records.

section may also define the return codes as 77-level data items.Alternatively, thesecodes can be specified as literals in the MOVE instruction.(MOVE literal toRETURN-CODE.) Note that RETURN-CODE is the name of a predefined storage area inCOBOL used to pass return codes to the sort; RETURN-CODE should not be defined inthe exit routine.

.34 Programmer'sGuide

The PROCEDURE DIVISION

the USING option ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an the PROCEDURE DIVISION header.Each identifierspecified after USING must be the same as those described in the 01-level of the LINK-AGE SECTION.Taking for example the identifiers defined in the fixed length recordLINKAGE SECTION shown here, they would appear as: PROCEDURE DIVISION US-ING EXIT-STATUS, RECORD-UP, WORK, IN-BUF, DUMMY1, DUMMY2, DUMMY3,DUMMY4, COM-LEN, COMMUNICATION-AREA.

GOBACK statement is used to return control to SyncSort.Do not use the EXITstatement as it will cause unpredictable results.Be sure that SyncSort receives a validreturn code before the GOBACK statement is executed.

-STATUS Codes (Fixed and Variable Length Records)

Record.SyncSort uses this Code to indicate the first call to the COBOLexit and that the first record to leave Phase 3 is in the RECORD-UP area.Most records.This is used for all calls except the first one when there are re-cords in the RECORD-UP arehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aa.After Code 00 has been issued, Code 04 ispassed to the exit until there is no record for the sort to pass to theRECORD-UP area.

records passed.This indicates that the last record has already been proc-essed by the exit.Do not attempt to reference the record again.No more re-cords will be passed to the exit routine.Note that if SyncSort is not passingany records to Phase 3, 08 will be passed every time including the first time.

-CODE Codes (Fixed and Variable Length Records)

this record.This instructs SyncSort to accept the (unaltered) record inthe RECORD-UP area.

this record.SyncSort will delete the current record in the RECORD-UParea.

E35. This instructs SyncSort to process any remaining recordswithout showing them to the E35 exit.Register 1 is ignored for processing thisreturn code.

this return code is used at end-of-fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aile (signalled by EXIT-STATUSLAST-TIME), it indicates that the E35 is also finished and will not add addi-tional records. When used before end-of-file, it indicates that SyncSort shouldprocess the &quot;current&quot; record passed to the E35, and any subsequent records,as if there were no E35 present. Note that when SyncSort is not creating anyoutput files (SORTOUT or SORTOFxx) and E35 is the only &quot;output,&quot; SyncSortterminates immediately, since any subsequent records will never be seen.Also

7. The Coding and Use of Exit Programs7.35

note that if an XSUM data set was being created, it will only contain recordsgenerated prior to the return code of 8.

a record.This instructs SyncSort to add the record in the WORK areato the input data set just ahead of the current record in the RECORD-UP area.When SyncSort returns control to the E35, the same record will be inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a theRECORD-UP area.The exit routine can then add another record from theWORK area or process the current record in RECORD-UP.

SyncSort.SyncSort will terminate and return to the calling pro-gram or the Supervisor.SyncSort will issue a completion code of 16 to indicatethat the sort was unsuccessful.

current record.SyncSort will replace the current record in theRECORD-UP area with the record in the WORK area.Be sure that the recordin the WORK area is valid before passing it to SyncSort.

Change a Record

order to change the record in the RECORD-UP area, first move it to the WORK area.Make the changes there and then pass return code 20 in RETURN-CODE.The alteredrecord in the WORK area will replace the record in RECORD-UP.

.36 Programmer'sGuide

Sample COBOL E35,Fixed Length Records

DIVISION.PROGRAM-ID. E35FL101.ENVIRONMENT DIVISIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aON.CONFIGURATION SECTION.SOURCE-COMPUTER. IBM-370.OBJECT-COMPUTER. IBM-370.INPUT-OUTPUT SECTION.FILE-CONTROL.I-O-CONTROL.DATA DIVISION.FILE SECTION.

-STORAGE SECTION.01 EVEN-FLAG01       01

-RETURN-CODE88ACCEPT-REC88DELETE-REC88END-EXIT88INSERT-REC88END-SORT88REPL-RECCHANGE-REC.05C-REC05C-INCR05C-BLANK

(2)PIC9(8)

://www.wendangwang.comPUTATIONAL.VALUE 0.VALUE 4.VALUE 8.VALUE12.VALUE16.VALUE20.VALUE'CHANGE'.VALUEZERO.VALUESPACES.VALUE'INSERT'.VALUEZERO.VALUESPACES.VALUE'E35'.VALUE0.

(6) PIC9(4) PICX(90)PICX(6) PIC9(4) PICX(90)

INSRT-REC. 05I-REC 05I-INCR 05I-BLANK

TOTAL. 05BLANKSPICX(10) 05TITLPICX(25)

'TOTAL RECORDS HANDLED'.

COUNTERPIC9(8)

7. The Coding and Use of Exit Programs7.37

Sample COBOL E35, Fixed Length Records (Continued)

SECTION.01 EXIT-STATUS 88FIRST-TIME 88MOST-TIME 88LAST-TIME01  http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a01  01  01

-UP.05RUWORK.05WKIN-BUF.05IBDUMMY1

(8)

.VALUE00.VALUE04.VALUE08.

(100).PICX(100).PICX(100).PICX(4).

DIVISION USING EXIT-STATUS, RECORD-UP, WORK,

-BUF, DUMMY.

NOT FIRST-TIME

1 TO COUNTER

0 TO RETURN-CODE.IF COUNTER LESS THAN 50

1 TO I-INCR

INSRT-REC TO WORKMOVE 12 TO RETURN-CODEGO TO RETURN-TO-SORT.IF COUNTER LESS THAN 75

1 TO C-INCR

CHANGE-REC TO WORKMOVE 20 TO RETURN-CODEGO TO RETURN-TO-SORT.

.38 Programmer'sGuide

Sample COBOL E35, Fixed Length Records (Continued)

COUNTER LESS THAN 100

1 TO I-INCR

INSRT-REC TO WORKMOVE 12 TO RETURN-CODEGO TO RETURN-TO-SORT.IF COUNTER LESS THAN 200

4 TO RETURN-CODEGO TO RETURN-TO-SORT.

-TO-SORT.

LAST-TIME MOVE 8 TO RETURN-CODE DISPLAYTOTAL. GOBACKhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.

7. The Coding and Use of Exit Programs7.39

Sample COBOL E35, Variable Length Records

DIVISION.PROGRAM-ID. E35VL101.ENVIRONMENT DIVISION.CONFIGURATION SECTION.SOURCE-COMPUTER. IBM-370.OBJECT-COMPUTER. IBM-370.INPUT-OUTPUT SECTION.FILE-CONTROL.I-O-CONTROL.DATA DIVISION.FILE SECTION.

-STORAGE SECTION.01EVEN-FLAG01

-RETURN-CODE88ACCEPT-REC88DELETE-REC88END-EXIT88INSERT-REC88END-SORT88REPL-REC

VALUE VALUE VALUEVALUEVALUE

9(2) VALUE ZERO.PIC 9(8) COMPUTATIONAL.0.4.8.12.16.20.

(6)VALUE'CHANGE'.PIC9(4)VALUEZERO.PIC X(90) VALUE SPACES.PICX(6)VALUE'INSERT'.PICX(4)VALUEZERO.PIC X(90) VALUE SPACES.

CHANGE-REC. 05C-REC 05C-INCR

C-BLANK01 INSRT-REC. 05I-REC 05I-INCR

I-BLANK

TOTAL.

BLANKSPIC X(10) VALUE ' E35'. 05TITLPICX(25)

'TOTAL RECORDS HANDLED'.

COUNTERPIC9(8)VALUEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a0.

.40 Programmer'sGuide

Sample COBOL E35, Variable Length Records (Continued)

SECTION.01 EXIT-STATUS 88FIRST-TIME 88MOST-TIME 88LAST-TIME

RECORD-UP.

RU OCCURS1TO100TIMES

ON LEN-RU

WORK.

WK OCCURS1TO100TIMES

ON LEN-WK

IN-BUF.

IB OCCURS1TO100TIMES

ON LEN-IB0101 01 01

PIC X(4).LEN-RULEN-WKLEN-IB

(8) COMPUTATIONAL.

.VALUE04.VALUE08.

X.

X.

X.

(8) COMPUTATIONAL.PIC9(8) COMPUTATIONAL.PIC9(8) COMPUTATIONAL.

7. The Coding and Use of Exit Programs7.41

Sample COBOL E35, Variable Length Records (Continued)

DIVISION USING EXIT-STATUS, RECORD-UP, WORK,

-BUF, DUMMY, LEN-RU, LEN-WK, LEN-IB.

NOT FIRST-TIME

1 TO COUNTER

0 TO RETURN-CODE.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aF COUNTER LESS THAN 50

54 TO LEN-WKADD 1 TO I-INCR

INSRT-REC TO WORKMOVE 12 TO RETURN-CODEGO TO RETURN-TO-SORT.IF COUNTER LESS THAN 75

44 TO LEN-WKADD 1 TO C-INCR

CHANGE-REC TO WORKMOVE 20 TO RETURN-CODEGO TO RETURN-TO-SORT.IF COUNTER LESS THAN 100

80 TO LEN-WKADD 1 TO I-INCR

INSRT-REC TO WORKMOVE 12 TO RETURN-CODEGO TO RETURN-TO-SORT.IF COUNTER LESS THAN 200

4 TO RETURN-CODEGO TO RETURN-TO-SORT.

-TO-SORT.

LAST-TIME MOVE 8 TO RETURN-CODE DISPLAYTOTAL. GOBACK.

.42 Programmer'sGuide

Coding a C E35 Exit Routine

C E35 exit program is indicated by the MODS control statement. An E35 exit cannotbe coded in C when running Tape Sort.

any other E35 exit routine, the C E35 exit routine is called each time a record isbrought out of Phase http://www.wendangwang.communication between SyncSort and the C http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aexit takes placethrough arguments defined in the function header. For example, records are passed to theC routineby an address presented in the second argument in the function parameter list.No storage is reserved in the exit program because the records exist elsewhere.

C E35 exit routine can be written using either the C370 V2R1 compiler with theV2R2 C370 Library, the SAA AD/Cycle C370 V1R2 Compiler and Library or the C/C  for MVS/ESA V3R1.1 Compiler and Library.When using the LE/370 run time librarymodules, it may be necessary to account for this additional storage by adjusting the bvalue of the Exit-Name parameter on the MODS statement.

Communication

parameter list structure required for passing fixed length and variable length recordsbetween the sort and the exit is detailed in the following section. The parameter namesused in the examples are arbitrary but each definition is required. Completehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a sample pro-grams showing the use of the argument lists are presented following the discussion of theexit interface.

Length Records - Function Definition

E35exit (int* exit_status, struct_ru*record_up, struct_ins_rep*work, struct_in_buf*in_buf,

* dummy1, int* dummy2, int* dummy3, int* dummy4,

*comm_len, struct_ca*communication_area)The following describes the parameters used in the preceding definition.exit_status

parameter points to a variable containing one of the fol-lowing exit status codes:00

record.SyncSort uses this Code to indicate

first call to the C exit and that the first recordto leave Phase 3 is in the record_up area. If thereare no records to pass to the exit, a 08 status willbe passed to the exit on the first call.

7. The Coding and Use of Exit Programs7.43

record_up

_buf

- dummy4http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

_len

_area

.44 Programmer'sGuide

records.This is used for all calls except thefirst one when there are records in the record_uparea. After Code 00 has been issued, Code 04 ispassed to the exit until there is no record for thesort to pass to the record_up area.

records passed.This indicates that the last re-cord has already been processed by the exit. Do notattempt to reference the record again. No more re-cords will be passed to the exit routine. Note thatif SyncSort is not passing any records to Phase 3,08 will be passed every time including the firsttime.

record_up parameter contains a pointer to the recordleaving Phase 3. The struct_ru data type represents a struc-ture that describes the fields within the record.

work parameter contains a pointer to a work area that isto be used to hold an inserted or replaced record returnedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a fromthe E35. The struct_ins_rep data type represents a structurethat describes the fields within the inserted or replaced re-cord.

in_buf parameter contains a pointer to the record thatSyncSort is to put in the output data set. Until a record hasbeen accepted or inserted, this pointer will be null. A recordat this address can be modified if required.

.Theyareusedwith variable length C E35 communication. Their definitionhere allows a common parameter list for fixed and variablelength C E15 and E35 exits.

parameter points to a variable that defines the commu-nication area length.

communication_area parameter contains a pointer to thecommunication area. The struct_ca data type represents astructure that describes the fields in the communication area.

Variable Length Records - Function Definition

E35exit (int* exit_status, void*record_uhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ap, void*work, void*in_buf, int*dummy1, int*len_ru, int*len_wk, int*len_ib, int*comm_len, struct_ca*communication_area)

following describes the parameters used in the preceding definition.exit_status

parameter points to a variable containing exit status

.See the exit_status definition for a fixed length C E35exit for the code definitions.

record_up parameter contains a &quot;universal&quot; pointer to therecord leaving Phase 3. The void* pointer can be cast to pointan appropriate structure to describe the record passed to theexit. This allows different record structures, as is commonwith variable length records, to share a universal pointer.The work parameter contains a &quot;universal&quot; pointer to a workarea that is to be used to hold an inserted or replaced recordreturned from the E35. The void* pointer can be cast to pointan appropriate structure to describe the work record.The inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a_buf parameter contains a &quot;universal&quot; pointer to therecord that SyncSort is to put in the output data set.Until arecord has been accepted or inserted, this pointer will be null.The void* pointer can be cast to point an appropriate structureto describe the work record.

parameter defines an unused place holder.

parameter points to a variable that defines the length ofthe record leaving Phase 3.This is the length of the recordreferred to in the record_up parameter.

parameter points to a variable that defines the length ofthe record to be inserted or used as a replacement for the

_up

_buf

len_ru

_wk

7. The Coding and Use of Exit Programs7.45

record_up record. This is the length of the record referred toin the work parameter.

_ib

parameter points to a variable that defines the length ofthe http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arecord that SyncSort is to put in the output data set.Thisis the length of the record referred to in the in_buf parameter.This parameter points to a variable that defines the commu-nication area length.

communication_area parameter contains a pointer to thecommunication area. The struct_ca data type represents astructure that describes the fields in the communication area.

_len

_area

-CODE Codes (Fixed and Variable Length Records)

this record.This instructs SyncSort to accept the (unaltered) record inthe record_up area.

this record.SyncSort will delete the current record in the record_uparea.

E35.This instructs SyncSort to process any remaining recordswithout showing them to the E35 exit. When this return code is used at end-of-file (signalled by exit_status 08), it indicates that the E35 is also finishedand will not add adhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aditional records. When used before end-of-file, it indicatesthat SyncSort should process the &quot;current&quot; record passed to the E35, and anysubsequent records, as if there were no E35 present. Note that when SyncSortis not creating any output files (SORTOUT or SORTOFxx) and E35 is the only&quot;output,&quot; SyncSort terminates immediately,since any subsequent records willnever be seen.

a record.This instructs SyncSort to add the record in the work area tothe input data set just ahead of the current record in the record_up area. WhenSyncSort returns control to the E35, the same record will be in the record_uparea. The exit routinecan then add another recordfrom the work area orprocess the current record in record_up.

SyncSort. SyncSort will terminate and return to the calling programor the Supervisor. SyncSort will issue a completion code of 16 to indicate thatthe sort was unsuccessful.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeplace current record. SyncSort will replace the current record in therecord_up area with the record in the work area. Be sure that the record in thework area is valid before passing it to SyncSort.

.46 Programmer'sGuide

Change a Record

order to change the record in the record_up area, first move it to the provided workarea. Make the changes there and then pass return code 20. The altered record in thework area will replace the record in record_up.

C E35, Fixed Length Records

#define FIRST_TIME0#define MOST_TIME 4#define LAST_TIME 8#define ACCEPT_REC0#define DELETE_REC4#define END_EXIT8#define INSERT_REC12#define END_SORT16#define REPL_REC20#include &lt;decimal.h&gt;

_Packed struct record  charrec[6]; decimal(7,0)incr; charaddress[90]; t_ru;

counter,i_incr;#include &lt;stdio.h&gt;#include &lt;stdlib.h&gt;#inclhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aude &lt;string.h&gt;

SMPE35FB(int* exit_status,t_ru* record_up,t_ru* work,t_ru* in_buf,

* dummy1,int* dummy2,int* dummy3,int* dummy4,int* comm_len, void*communication_area)

return_code;

*text1=&quot;CHANGE&quot;;char *text2=&quot;INSERT&quot;;

(*exit_status != FIRST_TIME) counter  ; return_code=ACCEPT_REC;

7. The Coding and Use of Exit Programs7.47

Sample C E35, Fixed Length Records (Continued)

(counter&lt;50)  i_incr  ; work-&gt;incr=i_incr; strncpy(work-&gt;rec,text2,6); return_code=INSERT_REC; gotoreturn_to_sort;if (counter&lt;75)  work-&gt;incr=record_up-&gt;incr 1d; strncpy(work-&gt;rec,text1,6); return_code=REPL_REC; gotoreturn_to_sort;if (counter&lt;100)  i_incr  ; work-&gt;incr=i_incr; strncpy(work-&gt;rec,text2,6); return_code=INSERT_REC; gotoreturn_to_sort;if (counter&lt;200)  return_code=DELETE_REC; gotoreturn_to_sort;retuhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arn_to_sort: if(*exit_status==LAST_TIME) return_code=END_EXIT;

(&quot;E35 total number of records handled:%d&quot;,counter);

return(return_code);

.48 Programmer'sGuide

Sample C E35, Variable Length Records

#define FIRST_TIME0#define MOST_TIME 4#define LAST_TIME 8#define ACCEPT_REC0#define DELETE_REC4#define END_EXIT8#define INSERT_REC12#define END_SORT16#define REPL_REC20#define MAX_RLEN104

_Packed struct record1  charrec[6]; intincr; charaddress[MAX_RLEN-14]; t_ru1;

_Packed struct record2  chartitle[10]; intnumber; t_ru2;

counter,i_incr,i_number;#include &lt;stdio.h&gt;#include &lt;stdlib.h&gt;#include &lt;string.h&gt;

SMPE35VB(int* exit_status,void* record_up,void* work,void* in_buf,

* dummy,int* len_ru,int* len_wk,int* len_ib,int* comm_len, void*communication_area)

7. The Coding and Use of Exit Progrhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aams7.49

Sample C E35, Variable Length Records (Continued)

return_code;

*text1=&quot;CHANGE E35&quot;;char *text2=&quot;INSERT E35&quot;;t_ru1 * p_record1,*pwork1;t_ru2 * p_record2,*pwork2;

_record1 = (t_ru1 *)record_up;pwork1=(t_ru1 *)work;

_record2 = (t_ru2 *)record_up;pwork2=(t_ru2 *)work;

(* exit_status != FIRST_TIME) counter  ; return_code=ACCEPT_REC;if (counter&lt;50)

(*len_ru == 14)

*len_wk = 14;

_number  ; pwork2-&gt;number=i_number; strncpy(pwork2-&gt;title,text2,10); else

*len_wk = 54;

_incr  ; pwork1-&gt;incr=i_incr; strncpy(pwork1-&gt;rec,text2,6);  return_code=INSERT_REC; gotoreturn_to_sort;if (counter&lt;75)

(*len_ru == 14)

*len_wk = 14;

-&gt;number=p_record2-&gt;number 1; strncpy(pwork2-&gt;title,text1,10); else

*len_wk = 54;

-&gt;incr=p_rechttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aord1-&gt;incr 1; strncpy(pwork1-&gt;rec,text1,6);  return_code=REPL_REC; gotoreturn_to_sort;

.50 Programmer'sGuide

Sample C E35, Variable Length Records (Continued)

(counter&lt;100)

(*len_ru == 14)

*len_wk = 14;

_number  ; pwork2-&gt;number=i_number; strncpy(pwork2-&gt;title,text2,10); else

*len_wk = 80;

_incr  ; pwork1-&gt;incr=i_incr; strncpy(pwork1-&gt;rec,text2,6);  return_code=INSERT_REC; gotoreturn_to_sort;if (counter&lt;200)  return_code=DELETE_REC; gotoreturn_to_sort;return_to_sort:

(*exit_status==LAST_TIME)

return_code=END_EXIT;

(&quot;E35 total number of records handled:%d&quot;,counter);

(return_code);

E16-Taking Action on Insufficient Intermediate Storage

E16 is given control in the event that the input data set is unable to fit into inter-mediate storage.Therehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a is no parameter list.The E16 return code tells SyncSort how torespond to the insufficient SORTWK problem.

Codes

present records only.This instructs SyncSort to process only those recordspresently contained on the intermediate storage devices.The sort will receivemessage WER054I RCD IN xxxxxxxx, OUT yyyyyyyy if the data is read fromSORTIN directly, or WER055I INSERT xxxxxxxx, DELETE yyyyyyyy if thedata receives input exit (E14 or E15) or INCLUDE/OMIT processing.Themessage's RCD IN or INSERT xxxxxxxx figure indicates how many recordshave been sorted. For a sort with no exits or INCLUDE/OMIT processing, theremaining records may be sorted by running another job using the

7. The Coding and Use of Exit Programs

.51

SKIPREC=n parameter on the SORT control statement, skipping the xxxxxxxxnumber of records.The new sort will start just where the last one left off.Thefinal ouhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atput is obtained by running a MERGE with the two SORTOUT datasets.

to sort all records.This tells SyncSort to continue to read in records fromthe input data set.If there are very few records left, the sort may completesuccessfully.If there are too many records to continue the sort, SyncSort willterminate with a SORT CAPACITY EXCEEDED message.

SyncSort.SyncSort will terminate immediately with a SORT CA-PACITY EXCEEDED message.

E17, E27, and E37 - Closing Data Sets

exits are unusual in that they are entered only once, at the end of their associatedphase.Because of this, they may be efficiently used to clean up after other exit routines(e.g., to close data sets).There are no parameter lists or return codes for these exits.

E18, E38, and E39 - Checking Labels, Processing Read orWrite Errors, End-of-File Routines, Special VSAM Processing

ehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1axits are mainly used for I/O error recovery routines.However, they may also beused to check labels, to do end-of-file processing, and to provide various information to theVSAM access method.

E18 and E38 Programs

E18 is only used for sorts and exit E38 only for merges or copies.Each exit is enteredexactly once, at the start of SORTIN processing.At this time, SyncSort checks Register1 for the address of a user parameter list specifying the various open and error exit rou-tines the user wishes SyncSort to include.SyncSort will then enter these routines at theappropriate times during execution.Because use to these exits forces the use of BSAMfor the input file(s), performance may be adversely affected.

format of the parameter list is given below.More information on the DCB fields canbe found in the appropriate IBM publication.

.52 Programmer'sGuide

Byte 1Byte 2Byte 3Byte 4

SYhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aNAD field

EXLST field

EROPT code

EODAD field

.Parameter List for E18 and E38

parameter list must begin on a fullword boundary and consist of an integral numberof words.With the exception of the required fullword of zeros used to indicate the endof the parameter list, entries are optional.The first byte of each word identifies the pa-rameter:SYNADfield

by 01 in byte 1.The SYNAD field contains the address of asynchronous read error routine, assembled as part of the exit program.Note that you may not use Register 13 as a save area pointer on entryto your routine.You must either provide your own save area or use theSYNADAF macro instruction.

by 02 in byte 1.The EXLST field contains the address of alist of pointers to user routines that perform operations such as labelchecking.Note that in the event that the list contains a DCB-exithttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aentry, it will not be entered during concatenated SORTIN processing.Indicated by 03 in byte 1.Bytes 2 and 3 contain zeros, byte 4 theEROPT code.This code tells SyncSort what action to take if it discov-ers an uncorrectable read error on a non-VSAM input file.X'00'

the EROPT code in the DCB parameter of theDD statement that describes the data set containingthe error.

the program.

the block containing the error.Accept the block containing the error.

7. The Coding and Use of Exit Programs

.53

'20'X'40'X'80'

EODADfield

by 04 in byte 1.The EODAD field contains the address ofan end-of-file routine.It can only be used with an E18 exit.

Input to E18 and E38

VSAM input, these exits can be used to pass the addresses of various VSAM exitsor to insert passwords into VSAM input ACB's.Whehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an control is returned to the sort,Register 1 must contain the address of a parameter list:

'05'X'06'

byte address of VSAM exit list3-byte address of password list

'0'Fullword of zeros

.

VSAM Parameter List for E18 and E38

both address entries are present, they may be in either order.Only one need be pres-ent.(QSAM parameters will be ignored.)The password list referenced in the parameterlist is found in the exit routine and is formatted as follows:2 bytes on a halfword boundary:

n of entries in list

by n 16-byte entries:

-byteDDname8-bytePassword

exit routine must not alter this list.The sort may destroy the last byte of the DDname field.

exit list is built using the VSAM EXLST macro, which provides the addresses of theVSAM exit routines.VSAM branches directly to the routines which must return to VSAMvia the addhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aress in Register 14.

do EODAD processing with E38, write a LERAD exit and check for X'04' in the FDBKfield of the RPL:this indicates input EOD.This field is needed by the merge, so it shouldnot be altered when returning to VSAM.

following example shows how to code the return to the sort.

.54 Programmer'sGuide

E18

PWDLST

://www.wendangwang.comSTLMBRCNOPDC DCDCDCDCDC DCDCDCDCDCDCDC...

...............

,PARMLST1,24(13)R13 points to sort's save area14,12,12(13)140,4X'01'

(BSAMERR)X'02'

(EXLST)X'03'

'000080' EROPTcodeX'04'

(BSAMEOD)X'05'

(VSAMEXL)X'06'

(PWDLST)A(0)

=SYNAD,LERAD=LERADH'2'

'SORTIN'

'INPASS'SORTINpasswordCL8'SORTOUT'SORTOUTddnameCL8'OUTPASS'SORTOUTpassword

synch error rtnVSAM logic errhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aor rtnBSAM error rtn

address listBSAM end of data rtnFigure181.

E18 Program

E39 Programs

E39 is used mainly for SORTOUT write error routines.The exit is entered once atthe beginning of merge or copy processing or the start of sort Phase 3.At this timeSyncSort checks Register 1 for the address of a user parameter list specifying the variousroutines the user wishes SyncSort to include.SyncSort will then enter these routines at

7. The Coding and Use of Exit Programs7.55

the appropriate times during execution.The use of an E39 exit forces the use of BSAMon the output file; this may degrade performance somewhat.The format of the parameter list is given below.

1010200

Table27.Byte 2

3SYNAD fieldEXLST field

List for E39

Byte 4

parameter list must begin on a fullword boundary and consisthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a of an integral numberof words.With the exception of the required fullword of zeros used to indicate the endof the parameter list, entries are optional.The first byte of each word identifies the pa-rameter:SYNADfield

by 01 in byte 1.The SYNAD field contains the address of asynchronous write error routine, assembled as part of the exit program.Note that you may not use Register 13 as a save area pointer on entry toyour routine.You must either provide your own save area or use theSYNADAF macro instruction.

by 02 in byte 1.The EXLST field contains the address of a listof pointers to user routines that perform operations such as label check-ing.If the EXLST field is specified, CHECKPOINT processing will notbe performed by SyncSort.

E39 may be used to supply a VSAM exit list or password list for the output file inthe same manner as described for exits E18 and E38.Note that http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aunlike E18 there is noEODAD field with this exit.

E61 - Modifying the Collating Process

61 is used to alter the collating of all control fields specified as having an o (order)value of E in the SORT/MERGE control statement.Note that an E61 exit routine is calledin Phase 1 for sort applications and in Phase 3 for merge applications.Each timeSyncSort encounters an order E control field, it moves a copy of the control field to a workarea and passes the copy's address to the exit routine.Thus, the E61 exit programprocesses a control field image while leaving the original control field intact.An orderE control field is collated in ascending order according to its f (format) code and its E61image.In order to code an effective E61 routine, the user must be familiar with thestandard data formats used by the operating system.

all order E control fields except BInary fields, the number of bytes in the contrhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aol fieldimage will be the number specified as the l (length) value on the SORT/MERGE control

.56 Programmer'sGuide

statement.BInary fields are left and right padded with zeros to the nearest byteboundary.For example, a control field designated as 5.3,1.4,BI,E receives three bits ofpadding on the left, one on the right, producing an image 2 bytes long.

E61 exit can process only the first 256 bytes of the control field image in a single pass.If a control field image is more than 256 bytes long, the exit will be entered more thanonce for that control field.

AC is specified as the format of a control field on the SORT or MERGE statement,SyncSort will translate the field to ASCII before the E61 routine is given control.In orderto use an E61 routine to modify what would be an AC control field, specify the field asCH in the SORT or MERGE statement and translate the image to ASCII after it is alteredby http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe E61 exit routine.

is no advantage to coding an E61 exit if the ALTSEQ control statement can providethe needed collating modification.ALTSEQ changes the installation's alternate collatingsequence, used for all control fields specified with the format code AQ.An E61 exit cannot be used with locale processing (LOCALE option enabled).

Parameter List

time your routine is executed, SyncSort will place the address of a three-word pa-rameter list in Register 1.The parameter list will be on a fullword boundary.The firstword contains the number of the control field within the record in byte 4.The secondword contains the address of the control field in the work area in bytes 2, 3, and 4.Thethird word contains the length of the control field in bytes 3 and 4.All values are givenin hexadecimal and the unused bytes are filled with zeros.

1000000

Table28.Byte 200

300

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aByte 4Number of control

of control field in work area

of control field

List for E61

a Control Field Image

length of the control field image is completely determined by the length and formatcode of the control field.Therefore, in order to provide a 12-byte PD image of 5 bytes fromthe original record, it is necessary for the SORT/MERGE control statement to referencea 12-byte PD control field that contains the 5 desired bytes.The extra 7 bytes are usedto contain the &quot;lengthened&quot; image.

7. The Coding and Use of Exit Programs7.57

Shortening a Control Field Image

length of the control field image is completely determined by the length and formatcode of the control field.To shorten a control field image, specify the full length of theoriginal control field as the l (length) value in the SORT/MERGE control shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atatement.Thenshorten each image by the same number of bytes and pad it uniformly to the length of theoriginal field.Be sure to pad each control field image with the same leading or trailingcharacter, and replace data in the control field image with the same type of data as thatin the actual control field.

a Collating Sequence

order E control field is collated according to its image and format code, in ascendingorder.To collate the field in apparent descending order, complement the control fieldimage according to its format code before returning control to SyncSort.For a BI or CHfield, for example, complement the image with hexadecimal FF's before returning controlto the sort.

REXX Exits

exit routines E15 and E35 can be coded in REXX.

Variables Provided by SyncSort MVS

MVS provides a number of special REXX variables to facilitate the developmentof REXhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aX exits. These variables offer a simple, efficient means of establishing communi-cation between the exit and the sort/merge.

load these variables, the following command must be used when the exit is called.

'SYNCREXX' 'GIVE'

the exit completes its work, the exit should use the following sequence of commandsto return the variables to SyncSort MVS.

'SYNCREXX' 'TAKE'RETURN

.58 Programmer'sGuide

The following table describes the special REXX variables.

the exit is entered, SYRECORD contains the current datarecord. The exit can accept the record, modify it or add a new record;SYACTION should be set accordingly.

SYRECORD is null, then SyncSort MVS has no data remaining.When this happens, the exit can either CLOSE or continue to IN-SERT new records.

variable must be set befhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aore the exit returns control to SyncSortMVS. It describes the disposition of the current record.Possiblevalues for SYACTION are as follows:ACCEPT:REPLACE:

the current record with no modification.Replace the current record with the contents of theSYRECORD.

the current record.

the contents of the SYRECORD before thecurrent record.

not return to the exit.Terminate SyncSort MVS.

:INSERT:

:ABEND:

an E15 is providing all the input (SORTIN not present), the onlyvalid values for SYACTION are INSERT, CLOSE or ABEND.

... ...SYGBLN8

variable will automatically be set to E15 or E35, depending onwhich type of exit is being called.

eight special variables are global variables. The user may setthese to any value provided that the value does not exceed 15

in length. SyncSort MVS will insure that thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aese variablesare preserved across calls to the exit.

is an additional global variable. The user may set this to anyvalue, provided the string does not exceed 1024 characters inlength. SyncSort MVS will insure that this variable is preservedacross calls to the exit.Table29.

Variables Provided by SyncSort MVS

7. The Coding and Use of Exit Programs7.59

Sample REXX Exit

following example illustrates a REXX exit that will count the number of records thatare passed to the exit:

'SYNCREXX' 'GIVE'

sygbln1='SYGBLN1' then sygbln1=0if LENGTH(syrecord) &gt; 0thendo

='REPLACE'sygbln1=sygbln1   1endelsedo

='CLOSE'

'REXX' syexityp 'counted' sygbln1 'records'end

'SYNCREXX' 'TAKE'return

.

REXX Exit Code

.60 Programmer'sGuide

Chapter 8.The Fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1alow of the Sort

chapter briefly outlines the flow of control in the standard Disk Sort, incore sort,merge and copy.It describes the order in which SyncSort will process and act on thePARMs, control statements and exit routines provided by the user.Note that all exe-cutions begin with Phase 0 processing and that a given SyncSort execution will skip stepswhere appropriate (e.g., will skip a &quot;Variable length record sampling&quot; step if sorting fixedlength records or HISTOGRM length values are supplied).No attempt has been madeto indicate which steps are required of all Disk Sorts, incore sorts, etc., or to indicate thenature or timing of any abend processing.

PARMs, merging EXEC and $ORTPARM PARM specifications.The EXECstatement/invoking program's parameter list overrides the installation defaults.$ORTPARM overrides the EXEC statement/invoking program's parameter list.Process cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1antrol statements (from the $ORTPARM DD statement and either theSYSIN DD statement or the invoking program's parameter list).Link-edit user exits (if necessary).

SORTIN/SORTINnn and SORTOUT/SORTOFxx/SORTOFx/SORTXSUMDCB attributes.

8. The Flow of the Sort8.1

MERGE or COPY, GO TO          →

-SortingPhase3

Variable length record sampling:open SORTIN, do the sampling, close SORTIN. GO TO           →

Load Phase 1 exits.  CallE11.  CallE18.  OpenSORTIN.

Perform SKIPREC processing.

the record level: Read from SORTIN.  CallE15.

Perform INCLUDE/OMIT processing. Perform INREC processing. Perform STOPAFT processing.  CallE61.

Perform SUM processing.

.

CallE16.  CloseSORTIN.

.

.2 Programmer'sGuide

1

there is sufficient mehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amory, GO TO         →

Sort

Delete Phase 1 exits.

all strings can be merged at once, GO TO     →

TO          →

2

Phase 1 exits.Load Phase 3 exits.CallE31.CallE39.OpenSORTOUT.On the record level:

.

to SORTOUT.

.CallE37.

Phase 3 exits.

TO           →

8. The Flow of the Sort8.3

Phase2

Phase 2 exits.CallE21.

the record level:

.

SUM processing.

.

Phase 2 exits.

TO           →

Phase 3 exits.Takecheckpoint.CallE31.CallE39.

SORTOUT, SORTOFxx, SORTOFx anhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad SORTXSUM.On the record level:

SUM processing.Write to SORTXSUM.Perform OUTREC processing.CallE35.

SORTOUT, SORTOFxx or SORTOFx are present, then for each output data set:

Perform STARTREC/ENDREC processing.

.4 Programmer'sGuide

INCLUDE/OMIT parameter processing.Perform SortWriter functions.Perform OUTREC processing.

ANSI control character processing.Write to SORTOUT, SORTOFxx, or SORTOFx.

.

all data sets.Delete Phase 3 exits.

TO           →

-SortingPhase3

user exits for the merge/copy.CallE31.CallE38.CallE39.

all data sets.

SKIPREC processing (for a copy).On the record level:

from SORTIN/SORTINnn or (for a merge) call E32 for a record.Call E15 (for a copy).

http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aINCLUDE/OMIT processing.Perform INREC processing.

STOPAFT processing (for a copy).Call E61 (for a merge).

8. The Flow of the Sort8.5

SUM processing (for a merge).Write to SORTXSUM (for a merge).Perform OUTREC processing.CallE35.

SORTOUT, SORTOFxx or SORTOFx are present, then for each output file:  Perform STATREC/ENDREC processing. Perform INCLUDE/OMIT parameter processing. Perform SortWriter functions. Perform OUTREC processing.

Perform ANSI control character processing.

to SORTOUT, SORTOFxx or SORTOFx.

CallE37.

Close all data sets.

user exits.

TO

→  Program Termination

Print SyncSort messages.

.

.6 Programmer'sGuide

Chapter 9.MAXSORT

: A Maximum Capacity Sort

is a maximum capacity shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aort designed to sort amounts of data that are toolarge for an ordinary sorting technique to process.

breaks up the sorting process into small, individual sorts. At the end of eachindividual sort a natural breakpoint occurs. At this time, the sorted data is written outon intermediate storage devices and it becomes possible to stop the program without los-ing the results of the previous processing. At each breakpoint, an operator may interveneto change program options.

all the input to the sort has been read and has become individual sorted data sets,this output becomes input to one or more merges. If all the data sets can be merged atonce, one final merge is performed. If all the data sets cannot be merged at once, someof them will be combined in one or more intermediate merges. Then, when all the datasets can be merged at one time, the final merge is performed and the final sorted outputis produced.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarThe diagrams on the following two pages illustrate the MAXSORT technique.

9. MAXSORT9.1

[此处图片未下载成功]

9.2 Programmer'sGuide

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

Chapter 9. MAXSORT9.3

MAXSORT's Advantages

MAXSORT, overlarge sorts require tape work areas or force the user tosegment the input and execute multiple disk sorts.With MAXSORT, any input dataset can be handled by one sort execution using disk work space.

requires less disk space than ordinary sorts. Because MAXSORT storesthe output of each individual sort on tape, the same disk SORTWK files can be usedover and over again.

the output of each individual sort is a completely sorted data set, the originaljob may be interrupted for higher priority jobs without wasting processing time.If a system or program failure occurs, whatever data sets have alreadyhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a been producedare still usable. The job can be restarted at the last breakpoint, and all previouslyproduced data sets can be used without resorting.

Control Language

and Disk Sort have similar JCL requirements.To initiate MAXSORT usingjob control statements, specify PARM='MAXSORT' on the EXEC statement.A program-initiated sort requests MAXSORT by using a PARM card image in the data set definedby the $ORTPARM DD statement. In either case, it may be necessary to request addi-tional main storage in order to use the MAXSORT technique.

EXEC Statement

//stepname EXEC       PGM=SYNCSORT PGM=SORT

=IERRCO00   ,PARM='MAXSORT'PGM=IGHRCO00 PGM=ICEMAN

.MAXSORT EXEC Statement

Statements

's DD statement requirements are summarized in the following table. As many

three additional types of DD statements mahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ay be needed.Note that SORTWK filesmust be allocated only to disk devices.

.4 Programmer'sGuide

MAXSORT DD Statements

//$ORTPARM //SYSIN

to override PARM or control statement information.Control statement data set. Required unless the address of a24-bit or 31-bit extended parameter list is supplied by an in-voking program.

data set. Required unless all messages are routed toconsole.

work area definition. Required unless DYNALLOC isspecified or MAXSORT is restarted at a MERGE breakpoint.SORT input data set. Required unless there is an E15. Ig-nored if the invoking program supplies an inline E15 exitroutine; optional if the MODS statement activates an E15 exitroutine.

data set. Required unless there is an E35.Ignored ifthe invoking program supplies an inline E35 exit routine;optional if the MODS statement activates an E35 exit routine.Output data http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aset for records deleted by SUM.Required ifXSUM parameter used.

data set. Must be DASD. Required.Required if intermediate output is on tape.

if intermediate output is on disk or if intermediateoutput is on tape and DYNATAPE is not specified.

data set. Required if Checkpoint-Restart is used.Required if user exits are in SYSIN and if user exits are tobe linkage-edited at execution time.

//SYSOUT //SORTWKnn //SORTIN

//SORTOUT DD

//SORTXSUM //SORTBKPT //SORTOU00 //SORTOUnn //SORTCKPT //SORTMODS //SYSLIN //SYSLMOD //SYSUT1 //SYSPRINT //ddname

for exits unless the exit is inline inLINKLIB/JOBLIB/STEPLIB or in SYSIN.Table30.

DD Statements

the RELEASE=ON parameter is active (either via specification or by default) at theconclusion of the sort portion of a MAXSORT, most of the allocathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aed SORTWK space is free(however, in the case of invoked sorts or SORTWKs defined as OLD, the data set is re-turned to the size allocated at MAXSORT initiation rather than the minimum size pos-sible).

9. MAXSORT9.5

The SORTBKPT, SORTOU00, SORTOUnn and SORTCKPT DD statements are discussedbelow. Refer to “Chapter 4.JCL and Sample JCL/Control Statement Streams” for a dis-cussion of the other DD statements, which are specified for MAXSORT just as they wouldbe specified for Disk Sort.

DD Statement

required SORTBKPT statement defines the breakpoint data set on which the sortcontrol information is stored. At the end of each individual sort or merge, a breakpointis reached and the information in the breakpoint data set is automatically amended.However, when MAXSORT is program-invoked or when any exit other than an E35 exitis being used, breakpoints cannot be taken.Nevertheless, the SORTBKPThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a statementmust be specified for all MAXSORTs, even those for which a breakpoint restart is notpossible.

Disk Space for the Breakpoint Data Set

breakpoint data set must be allocated on a direct access device. It is recommendedthat space for the breakpoint data set be allocated in the job step preceding the sort step.Or, the breakpoint data set may be pre-allocated in a separate job.

Allocation of the Breakpoint Data Set

following example illustrates how disk space for a breakpoint data set might be al-located as part of a MAXSORT job control stream.These two statements would followthe JOB statement:

//ALLOC EXECPGM=IEFBR14//BKPTDATA DDDSN=BKPT.DATA,DISP=(NEW,CATLG),UNIT=SYSDA,// SPACE=(1000,(100,50))Figure184.

Job Step Allocating Disk Space for a Breakpoint Data Set

this example, the name of the breakpoint data set is BKPT.DATA. Because this datasethttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a must be kept until MAXSORT has completed, DISP=(NEW,CATLG) has been speci-fied. Supplying approximately 100K bytes of primary space and allowing for secondaryallocation should be adequate.

SORTBKPT DD Statement

sample SORTBKPT DD statement which follows identifies the breakpoint data setfor which disk space has already been allocated.

.6 Programmer'sGuide

//SORTBKPT DDDSN=BKPT.DATA,DISP=(OLD,KEEP)

SORTBKPT DD StatementFigure185.

SORTBKPT DD statement defines the breakpoint data set for which disk space has

been allocated. The data set name must be the same name which was specified

the space for the breakpoint data set was allocated. DISP=(OLD,KEEP) is specified

that this statement does not have to be changed if MAXSORT is restarted. The DCB

should not be coded because MAXSORT supplies these values. If a VOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aLSER

coded when the disk space for the breakpoint data set was allocated, the same

must be specified in the SORTBKPT DD statement.

DD Statement

SORTOU00 DD statement is required for every MAXSORT application in which the

output is stored on tape.

SORTOU00 DD statement defines the unit to be used for the output of the individual

and intermediate merges.MAXSORT will create and name these data sets which

eventually be merged to produce the final sorted output.

data set names generated will have one of the two formats.If the TIMESTMP option

not specified (the installation default), data set names will have the format:  Snn TDS.jobname.  Mnn

the TIMESMP option is specified at installation time, data set names will have theformat:

Snn TDS.Ddddhhmm.jobname.  Mnn

either case, thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe S or M indicates whether the output is from the sort phase or from the

phase; nn is the relative number of the data set (01 to 99). The Ddddhhmm time

refers to the time (Julian day, hour and minute) the sort began.The prefix default

(TDS.) can be changed by specifying the BKPTDSN PARM option.

following rules should be observed in coding the SORTOU00 DD statement:

9. MAXSORT9.7

Specify DISP=(NEW,KEEP) and a permanent DSNAME and VOL=PRIVATE so that

scratch tape is used and the volumes are unloaded. Failure to specify this can result

the rewinding of the scratch tape and overwriting of the intermediate sort output.

the DEFER option in the UNIT parameter so that mount messages to the

that do not pertain to MAXSORT are suppressed.

and SORTIN cannot share the same tape unit. However, SORTOU00 and

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarSORTOUT may share the same tape unit unless the DYNATAPE PARM is specified.

and SORTOUT may always share the same unit.

DYNATAPE is in effect, the tape unit name must be the same as the unit name

in the TAPENAME PARM.

SORTOU00 DD Statement//SORTOU00 DD DSN=PERM.OU00,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

.Sample SORTOU00 DD Statement

DD Statements

SORTOUnn DD statements allocate the tape units used as input to the merge phase.

are required unless the DYNATAPE option (available only under MVS) is used.

it is not necessary to specify the SORTOUnn DD statements when DYNATAPE

used, it is a good idea to pre-allocate at least two SORTOUnn data sets when the

option is specified. This ensures that the minimum required number of tape

will be available forhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the merge phase. When additional units are available,

will provide performance benefits.

following rules should be observed in coding the SORTOUnn DD statements:

At least two tape units must be allocated in the absence of DYNATAPE. However,

more units will make the merge phase complete more quickly.

statement must be allocated to a unique tape drive. If DYNATAPE is in effect,

tape unit name must be the same as the unit name specified in the TAPENAME

.

the tape units must operate at the same recording density. For best performance,

density units should be run at the highest density.

each SORTOUnn statement, replace the 'nn' with a two digit number between

and 99. The numbers need not be consecutive.

.8 Programmer'sGuide

Specify DISP=(NEW,KEEP), a permanent DSNAME and VOL=PRIVATEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a so that a

tape is used and the tape volumes are unloaded.

the DEFER option in the UNIT parameter so that mount messages to the

that do not pertain to MAXSORT are suppressed.

SORTOUnn DD Statements//SORTOU01 DD DSN=PERM.OU01,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU02 DD DSN=PERM.OU02,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

.Sample SORTOUnn DD Statements

Disk for Intermediate Output

most cases, tape units will be used to store the intermediate output of the individual

and intermediate merges. However, it may be desirable in some circumstances to

intermediate output on disk (e.g., to take advantage of a mass storage subsystem).

the intermediate output to a mass storage subsystem will not compromise the

's efficiency.Because these fihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ales will be written and read sequentially, paging will be

.

disk is used for intermediate storage, the following rules should be observed:

The SORTOU00 statement should not be coded.SORTOUnn statements may be allocated to real or MSS virtual volumes.To determine how many SORTOUnn DD statements to supply, divide the total

of bytes of sort input data by the number of bytes of SORTWK space and add

to the result. This figure is the number of SORTOUnn statements to supply. If too

SORTOUnn DD statements are supplied, MAXSORT will terminate for restart

the point at which a new DD statement is needed.

SORTOUnn DD statement must allocate enough primary and secondary space

hold all of the data written during that intermediate sort.

overflow is not supported for disk SORTOUnn data sets. Record lengths must

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at exceed the track capacity unless VS or VBS records are being processed.

9. MAXSORT9.9

SORTCKPT DD Statement

DD statement is required in order to restart a MAXSORT which is task-invoked orincludes a user exit routine because in these cases MAXSORT cannot be restarted froma breakpoint. The standard OS/VS Checkpoint-Restart feature is used. Both automaticCheckpoint-Restart and deferred Checkpoint-Restart capabilities are supported.(See“Chapter 12. Performance Considerations”) Checkpoints are taken at the end of eachintermediate sort or merge.

SORTBKPT DD statement must be specified in addition to the SORTCKPT DDstatement even when MAXSORT cannot be restarted from a breakpoint.

MAXSORT with an E35 exit does not require the SORTCKPT DD statement.

Statements

statements will only be accepted at the initial execution of MAXSORT. IfMAXSORT is restartedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a, the control statements cannot be changed.Except for MERGEand OUTFIL, all SyncSort control statements are fully supported for MAXSORT.

Options

MAXSORT parameters described below may be specified on the EXEC statement, the$ORTPARM DD statement, PARMTBLE or PARMEXIT, and may be listed in any order.BKPTDSN  cc...c. BKPTDSN =

BKPTDSN PARM is used to change the prefix of the data set names for the outputof the individual sorts and intermediate merges. TDS. is the delivered default. The lastcharacter of the prefix must be a period. If the TIMESTMP option was specified at in-stallation time, up to 21 characters may precede that period. Otherwise, up to 31 char-acters may be specified before the final period.

.10 Programmer'sGuide

DYNATAPE DYNATAPE

instructs MAXSORT to dynamically allocate any tapes needed as input for

merge phase.DYNATAPE may be usehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad instead of (or as a supplement to)

DD statements.

, the default, disables dynamic allocation.

parameter is required in order to execute MAXSORT.

MAXWKSP =     n

option specifies the maximum amount of disk SORTWK space that MAXSORT can

. When this parameter is used, MAXSORT will release excess space in order to meet

figure specified by the user.

the RELEASE=ON parameter is active (either via specification or by default) at the

of the sort portion of a MAXSORT, most of the allocated SORTWK space is

(however, in the case of invoked sorts or SORTWKs defined as OLD, the data set

returned to the size allocated at MAXSORT initiation rather than the minimum size

).

MAX, the default value, is specified, all primary and secondary space whihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ach has been

will be acquired. The MAXWKSP value may also be specified as a decimal

of cylinders (n) or as a decimal number of megabytes (nM) of work space.

9. MAXSORT9.11

If MAXWKSP is specified as n cylinders, MAXSORT will convert the specification to an

byte value. MAXSORT will multiply by n the capacity of a cylinder on the disk

to the lowest-numbered SORTWKnn DD statement.

:  MAXWKSP should be specified as greater than or equal to MINWKSP, if specified.

MINWKSP =     n

option specifies the minimum amount of disk SORTWK space that MAXSORT can

. If the MINWKSP value exceeds the primary allocation and sufficient secondary al-

cannot be obtained to meet the MINWKSP value at the time of execution, the sort

. It can be restarted later when more space is available.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arMINWKSP value may be specified as a decimal number of cylinders (n) or a decimal

of megabytes (nM) of work space.

default MINWKSP value is 8 cylinders.

MINWKSP is specified as n cylinders, MAXSORT will convert the specification to an

byte value. MAXSORT will multiply by n the capacity of a cylinder on the disk

to the lowest-numbered SORTWKnn DD statement.

: MINWKSP should be specified as less than or equal to MAXWKSP, if specified.

RESTART =     id

parameter specifies the point at which restart is to occur.

, the default value, requests that the sort start at the most recent breakpoint.

specifies that the SORTBKPT data set is to be cleared so that it can be used for a new

. (Be sure to specify NO only when the SORTBKPT data set is empty or should be

.)

.12 Programhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amer'sGuide

To restart at a particular breakpoint, code its id number.The breakpoint id number is

by message WER350I.

n SORTSIZE =  nM   nT

option is accepted but ignored.Its function has been replaced by SyncSort internal

.

n SORTTIME =

SORTTIME parameter terminates the sort at the next breakpoint after n minutes

clock time have elapsed. (The sort may be restarted later.) The default is 1440 minutes

(24 hours).

this parameter is omitted or 1440 is specified, the sort will not terminate prematurely.

parameter may be specified with operator communication at installation time. If

communication is specified, the sort will be interrupted at the next breakpoint

the specified amount of time has elapsed and the operator will be asked whether to

the sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at or continue until the next breakpoint.

name TAPENAME =    This parameter specifies the tape unit generic name for dynamic tape allocation.The

TAPENAME is TAPE.

9. MAXSORT9.13

If the TAPENAME parameter is specified, the same unit generic name must be specified

both the SORTOU00 and the SORTOUnn DD statements.

tape unit generic name must be a valid unit name at your installation.

Programs

the exits available for Disk Sort are supported for MAXSORT. However, since

never runs out of work space on even the largest sorts, an E16 exit routine

never be called. Exit routines may be written in COBOL, C, Assembler language, or

.All exits should be prelink-edited for maximum efficiency.

following rules must be observed when MAXSORT includes an exit routine:

Exit programs are nohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at allowed to take their own OS or VS checkpoints.MAXSORT may take system checkpoints when the following exits are active: E14,

, E25, E35 and E61. Since a checkpoint may be taken between any two calls of

exits, these routines should be coded accordingly. Any restrictions that apply

system Checkpoint-Restart, such as restrictions on the use of data sets, are appli-

to the coding of these exit routines.

MAXSORT from a Program

can be invoked from programs written in COBOL, PL/1 or Assembler lan-

. However, this is the least efficient method of executing MAXSORT and perform-

benefits will be realized if MAXSORT is initiated through job control language.

MAXSORT is invoked from a program, the MAXSORT PARM should be specified

the $ORTPARM DD statement. The SYSIN DD statement is ignored.

MAXSORT

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparA JCL-initiated MAXSORT can be restarted from a breakpoint if necessary.When

is restarted from a breakpoint, the following PARM options cannot be modi-

: CMP=CPD/CLC, EQUALS, E15/E35=COB, FILSZ, LOCALE, MAXSORT, STOPAFT

TAPENAME. Other PARM options will be accepted if they are specified on the EXEC

. Only the CORE parameter can be passed through $ORTPARM.

control statements cannot be modified when MAXSORT is restarted. However,

l5, l6 and l7 values on the LENGTH parameter of the RECORD control statement can

altered.

.14 Programmer'sGuide

Restarting MAXSORT with Exit Routines or an Invoked MAXSORT

MAXSORT includes an exit routine or is invoked from a program, it cannot be re-

from a breakpoint.Instead, it can be restarted from a checkpoint using the

OS/VS Checkpoint-Restart feature.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Checkpoints are taken at the end of each

sort or merge.

MAXSORT is restarted from a checkpoint, modified PARM options cannot be

on the EXEC statement. Only the CORE parameter can be passed through

$ORTPARM.

specify that checkpoints be taken for a MAXSORT with an exit routine or for an in-

MAXSORT, the following rules must be observed:

Include the SORTCKPT DD statement in the JCL (in addition to the SORTBKPT

statement.

a permanent data set name to every SORTWKnn DD statement and specify

=(NEW,DELETE,KEEP).

RD=R and MSGLEVEL=1 on the JOB statement.

the CKPT parameter on the SORT/MERGE control statement.

's Operator Interface

MAXSORT's operator interface options are enabled when SyncSort is installed, they

permit operator communication at selectehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad breakpoints (e.g., at the first breakpoint

SORTTIME has expired, or when tape drives are dynamically allocated under

.)Operator communication allows the operator to examine the environment

execution time to decide whether or not to terminate MAXSORT at that breakpoint.

the operator decides to terminate the sort, it can be restarted later at that breakpoint.

the previously produced sorted data sets can be used without resorting.

communication with MAXSORT is not a delivered default - these options must

enabled at SyncSort installation time.

example, if MAXSORT's assigned block of computer time (its SORTTIME value) has

exhausted and SyncSort was installed to permit operator intervention at such times,

WER375D is generated.WER375D PAYROLL.SORTSTEP - MAXSORT BKPT PAYROLL S12

D TIME ESTIMATE: 30 MINUThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aES UNTIL NEXT NOTIFICATION

D REPLY 'GO' TO CONTINUE, 'STOP' TO TERMINATE

.Example: Operator Notification at SORTTIME Expiration

9. MAXSORT9.15

The operator receiving this message can decide to terminate the sort or allow it to con-

, basing his decision on scheduling priorities and the estimated time of the sort.

another 30 minutes have passed, the operator will be asked again whether or not

should be terminated.

DYNATAPE is specified and operator communication has been enabled at instal-

time, message WER376D may be generated to report the results of the dynamic

attempt.WER376D PAYROLL.SORTSTEP - MAXSORT BKPT PAYROLL.S01

D 4 TAPE UNITS ALLOCATED TO PAYROLL

D 6 TAPE UNITS NEEDED FOR BEST PERFORMANCE

D TIME ESTIMATE USING 4 TAPE UNITS--

D 20 MINUTEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aS TO NEXT BREAKPOINT

D REPLY 'GO' TO CONTINUE, 'STOP' TO TERMINATE, 'NN' # UNITS

.Example: Operator Notification with DYNATAPE

the operator responds 'GO', MAXSORT will execute with four tape units.If the oper-

responds 'STOP', MAXSORT will terminate.If the operator responds with a number

('NN'), MAXSORT will try to allocate that total number of tape drives. Ideally, the oper-

should specify six for 'NN' because MAXSORT needs six tape units for best per-

.If the operator requests additional tape units, message WER376D will be

. The operator will again be prompted for a 'GO', 'STOP' or 'NN' reply. In this

, the operator can balance the requirements of MAXSORT against the requirements

other jobs that are executing at the same time.

DYNATAPE is specified, there may not be enough tape units available for dyhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anamicallocation. In this case, message WER377D is generated.

D PAYROLL.SORTSTEP - MAXSORT BKPT PAYROLL.S01

D INSUFFICIANT TAPE UNITS AVAILABLE

D 2 TAPE UNITS ALLOCATED TO PAYROLL

D 4 TAPE UNITS NEEDED TO CONTINUE EXECUTION

D REPLY 'RETRY' TO GET UNITS, 'STOP' TO TERMINATE

.Example: Operator Notification of Insufficient Tape Units under

operator receiving message WER377D can wait until additional tape drives have

released and then reply 'RETRY'. Or, the operator can answer 'STOP' to terminate

job and then restart it later when more tape drives become available.

the DYNATAPE and TAPENAME PARMs have been specified and all tape units on the

within the TAPENAME class have already been allocated, message WER378D is

.

.16 Programmer'sGuide

WER378D NO ADDhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aITIONAL TAPE UNITS EXIST FOR GENERIC CLASS 2400-3

.Example: Operator Notification of Insufficient Tape Units for

Class

WER378D is followed by message WER376D if the number of tape drives allo-

is sufficient for execution, or by message WER377D if it is not sufficient.

9. MAXSORT9.17

Sample MAXSORT JCL/Control Streams

following examples illustrate how the JCL could be coded for typical 100-megabyte

.

1: A 1-Gigabyte MAXSORT with Only Minimal Disk Space Available

installation is running a 1-gigabyte sort and has a restricted amount of disk space

for SORTWK across three volumes (WORK1, WORK2 and WORK3).

JCL for this job follows.//ALLOC EXECPGM=IEFBR14

//BKPTDATA DDDSN=BKPT.DATA,DISP=(NEW,CATLG),

// UNIT=SYSDA,SPACE=(1000,(100,50))

//SORT EXECPGM=SYNCSORThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a,PARM='MAXSORT,MINWKSP=600'

//SORTBKPT DDDSN=BKPT.DATA,DISP=(OLD,KEEP)

//SYSOUT DD...

//SORTIN DD...

//SORTOUT DD ...

//SORTWK01 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),

// VOL=SER=WORK1

//SORTWK02 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),

// VOL=SER=WORK2

//SORTWK03 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),

// VOL=SER=WORK3

//SORTOU00 DDDSN=PERM.OU00,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU01 DDDSN=PERM.OU01,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU02 DDDSN=PERM.OU02,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU03 DDDSN=PERM.OU03,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SYSIN DD*

=(1,10,CH,A)

/*

.

.Sample JCL Control Stream for a 1-Gigabyte MAXSORT123456789This job step is run in order to allocate the disk spachttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae for the breakpoint data set via

utility program IEFBR14.

statement allocates the space for the breakpoint data set.

(NEW,CATLG) because this data set must be saved.Specify2.

.18 Programmer'sGuide

3.The EXEC statement initiates the regular SyncSort program, and the MAXSORT

is specified, as required. This job requests a minimum of 600 cylinders of diskspace for SORTWKnn data sets. If that much space cannot be obtained during thejob, the program will terminate.

SORTBKPT DD statement is required for all MAXSORTs. It identifies thebreakpoint data set which was allocated in the first job step.DISP=(OLD,KEEP) isspecified so that this statement can be reused if MAXSORT is restarted.

DD statements are coded just as they would be for an ordinary sort.

SORTWKnn DD statements must be allocated to disk or MAXSORT will termi-nate. In this case, 450 cyhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1alinders of primary space have been allocated. Secondary al-location could provide up to 300 cylinders on each volume if that amount of free spaceexists. Since the MINWKSP PARM specifies at least 600 cylinders, this program willterminate unless 150 cylinders of secondary space can be obtained.

SORTOU00 DD statement is required for this job because the intermediate sortoutput will be stored on tape. DISP=(NEW,KEEP), a permanent DSN andVOL=PRIVATE are specified to ensure that the system unloads each output tape.The DEFER option in the UNIT parameter is specified so that mount messages to theoperator that do not pertain to MAXSORT are suppressed.

SORTOU01, SORTOU02 and SORTOU03 DD statements allocate the tape unitsused as input to the merge phase. Permanent DSNAMEs, DISP=(NEW,KEEP),VOL=PRIVATE and the DEFER option in the UNIT parameter are all specified justas they were for the SORTOU00 DD statement.

sohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art control statements are included here.4.5.6.7.8.9.

9. MAXSORT9.19

Example 2: Restarting the MAXSORT in Example 1 from a Breakpoint

1 can be restarted from a breakpoint simply by submitting the original job con-trol stream without the job step which allocated space for the breakpoint data set. The jobwill be restarted from the last breakpoint because RESTART=LAST is the default; it isnot necessary to specify RESTART=LAST on the EXEC statement.

JCL for this job follows.//SORT EXECPGM=SYNCSORT,PARM='MAXSORT,MINWKSP=600'

//SORTBKPT DDDSN=BKPT.DATA,DISP=(OLD,KEEP)

//SYSOUT DD...

//SORTIN DD...

//SORTOUT DD ...

//SORTWK01 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK1

//SORTWK02 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK2

//SORTWK03 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK3

//SORTOU00 DDDSN=PERM.OU00,DISP=(NEW,KEEP),://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU01 DDDSN=PERM.OU01,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU02 DDDSN=PERM.OU02,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU03 DDDSN=PERM.OU03,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SYSIN DD*

=(1,10,CH,A)

/*

.Sample JCL Control Stream for Restarting a 1-Gigabyte MAXSORT

JCL is identical to the JCL in Example 1 except that the step which allocated thedisk space for the breakpoint data set is not resubmitted.

.20 Programmer'sGuide

Example 3: A 1-Gigabyte MAXSORT with Dynamic Tape Allocation

example is identical to Example 1 with one difference: the DYNATAPE PARM re-quests dynamic tape allocation.

JCL for this job follows.//ALLOC EXECPGM=IEFBR14

//BKPTDATA DDDSN=BKPT.DATA,DISP=(NEW,CATLG),UNIT=SYSDA,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

// SPACE=(1000,(100,50))

//SORT EXECPGM=SYNCSORT,PARM='MAXSORT,MINWKSP=600,

// DYNATAPE'

//SORTBKPT DDDSN=BKPT.DATA,DISP=(OLD,KEEP)

//SYSOUT DD...

//SORTIN DD...

//SORTOUT DD ...

//SORTWK01 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK1//SORTWK02 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK2//SORTWK03 DDUNIT=SYSDA,SPACE=(CYL,(150,20)),VOL=SER=WORK3//SORTOU00 DDDSN=PERM.OU00,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU01 DDDSN=PERM.OU01,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SORTOU02 DDDSN=PERM.OU02,DISP=(NEW,KEEP),

// UNIT=(TAPE,,DEFER),VOL=PRIVATE

//SYSIN DD*

=(1,10,CH,A)

/*

.Sample JCL Control Stream for a 1-Gigabyte MAXSORT

DYNATAPE PARM requests that tape units be obtained dynamically. BecauseDYNATAPE has been specified, the SORTOU01, SORTOU02 and Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aORTOU03 DD state-ments specified in Example 1 do not have to be supplied. They will be created and dy-namically allocated when needed. If enough tape units are available at the time the jobis run, the sort will be successfully completed in one step.

, there may not be enough tape devices available under dynamic allocation atexecution time. In that case, the job will terminate and can be restarted at a later timewhen more tape units are available.

best results, code two SORTOUnn DD statements in addition to specifying theDYNATAPE PARM as the above example illustrates. This approach ensures thatMAXSORT will have the minimum two tape units needed for the merge phase and alsoallows MAXSORT to take advantage of the additional tapes available under dynamic al-location.

9. MAXSORT9.21

Tuning MAXSORT

's performance can be optimized by controlling the intermediate sorts whichit http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aprocesses. A balance should be achieved between the number and duration of interme-diate sorts. Limiting the number of sorts reduces the required tape mounts and restrictingthe duration of sorts decreases the interval between breakpoints.

good rule of thumb is that each intermediate sorted data set should create from one tofive volumes of input data, and the only way to determine the amount of input data isby controlling the amount of SORTWK space used. This is illustrated in Figure195.1 tape volume contains 250 megabytes

3390 cylinder can hold approximately 800,000 bytes

: 750 megabytes (3 tape volumes)

: Each intermediate sort processes one input volume,

.e. 3 intermediate sorts should be run.

determine SORTWK allocation (for 3390 SORTWKs):

one input volume250,000,000

cylinder capacity800,000

: 313cylinders.

ensure 3 http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aintermediate sorts:

313 cylinders

=250M

195.CalculatingMAXWKSP

only 50 cylinders were allocated in the preceding example, 19 intermediate sorts wouldbe performed, increasing the required tape mounts and potential for error. If 800 cylin-ders were allocated, most of the input would be processed by the first intermediate sort,delaying the first breakpoint and introducing the potential for losing data. It is crucial,therefore, to allocate a balanced amount of DASD space that will divide your file intoreasonably sized segments to minimize the possibility of system error and to enhance yourperformance.

tuning MAXSORT then, a number of individual environmental elements shouldbe considered. A study of disk and tape availability, input data file size, and virtualstorage limitations will help you optimize the balance of performance and reliability.

.22 Programmerhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a'sGuide

Chapter 10.PARASORT

: Parallel Input Processing for Elapsed TimeImprovement

improves elapsed time performance for sorts whose input is a multi-volumetape data set and/or concatenated tape data sets.Reduced elapsed time can help criticalsort applications achieve batch window goals.

performance improvement from PARASORT is a result of processing the SORTINinput volumes in a parallel fashion.Depending upon the resources provided, elapsed timecan be reduced up to 20% for 2-way input and up to 33% for 4-way input.

requires additional tape units for the application.You will need from twoto eight times the current number of tape units, depending upon resource availability andthe degree of improvement desired. PARASORT automatically manages the tape unitsand minimizes the use of the tape drive resources by deallocating excess tape drivesduring initialization and relhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aeasing all the extra units at the end of the sort input phase.PARASORT Applicability

SyncSort facilities or application characteristics cannot be used with PARASORT.The following are incompatible with a PARASORT application:

A SORTIN record format (RECFM) of VS or VBS.An ASCII tape data set specified for SORTIN.

10. PARASORT10.1

An exit routine other than a pre-linked or inline E35 exit.EQUALS specified either as an installation or run-time option.SKIPREC or STOPAFT options specified.SEQNUM specified on INREC.CKPT (checkpoint) option in effect.The MAXSORT option specified.The OUTREC CONVERT feature to convert VL records to FL format.Certain unusual sort key types, feature combinations, or long sort keys in excess of

bytes.

=COPYspecified.

Control Language

JCL for PARAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSORT is similar to the JCL for a standard disk sort.The primarydifference is that PARASORT JCL must specify additional tape units to allow parallelinput processing of the SORTIN data set.For details on SORTIN JCL for PARASORT,see “SORTIN DD Statement with PARASORT” on page 10.3.

initiate PARASORT using job control statements, specify PARM='PARASORT' on theEXEC statement. A program initiated sort requests PARASORT by using a PARM cardimage in the data set defined by the $ORTPARM DD statement.

EXEC Statement  //stepname EXEC       PGM=SYNCSORT PGM=SORT PGM=IERRCO00   ,PARM='PARASORT'PGM=IGHRCO00 PGM=ICEMAN

.PARASORT EXEC Statement

Statements

's DD statement requirements are summarized in the following table.Oneadditional DD type (SORTPARn) is required compared to a conventional disk sort.

.2 Programmer'sGuide

PARASORT DD Statements

//$ORTPARM://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar

//SYSIN DDDDUsed to override PARM or control statement information.Control statement data set. Required unless the address of a

-bit or 31-bit extended parameter list is supplied by an in-

program.

data set. Required unless all messages are routed to

.

work area definition. Required unless DYNALLOC is

.

input data set. Required.

additional tape units for parallel reading of SORTIN.

.

data set. Required unless there is an E35.Ignored if

invoking program supplies an inline E35 exit routine;

if the MODS statement activates an E35 exit routine.

data set for records deleted by SUM.Required if

parameter used.

unless E35 user exit is in

/JOBLIB/STEPLIB.

.PARASORT DD Statements//SYSOUT //SORTWKnn //SORTINhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a //SORTPARn //SORTOUT DDDDDDDDDD//SORTXSUM //ddname DDDD

SORTIN and SORTPARn DD statements are discussed below.For a discussion ofthe other DD statements, which are specified for PARASORT just as for anon-PARASORT Disk Sort, see “Chapter 4.JCL and Sample JCL/Control StatementStreams”.SORTIN DD Statement with PARASORT

SORTIN DD statement is required for a PARASORT application. It must define ei-ther a single multi-volume tape data set or several concatenated tape data sets, which canbe single or multi-volume.If the SORTIN is concatenated, each data set must meet thenormal SORTIN concatenation requirements and must be able to use the same devicetype so that UNIT=AFF=SORTIN can be specified for all data sets in the concatenation.For a discussion of normal SORTIN JCL, see “Chapter 4.JCL and Sample JCL/ControlStatement Streams”

optimal performance, data sets that reside on tapes, such as 3480s, that can http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1abe readonly in a single direction should have two units allocated.If the data set is on a tape thatsupports bidirectional processing, a single unit is sufficient.In all cases DEFER mount-ing must be specified.

10. PARASORT10.3

SORTIN data sets may not be passed data sets or have PASS specified on their DDstatement.

the catalog or specific list of volume serial numbers must be specified. The volumeserial list must accurately reflect the volumes in the data set. If extra volumes are spec-ified (as may happen if an old data set is rewritten with less data) an error message willbe generated. A volume sequence number may not be specified.

following example SORTIN DD statements for PARASORT illustrate three differentSORTIN cases:

A multi-volume cataloged data setA multi-volume uncataloged data setConcatenated single and multi-volume uncataloged data sets

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ate that each example includes a y on the UNIT specification (for example,UNIT=(3480,y,DEFER)).The y is either 1 or 2 and indicates the number of units to beallocated for these devices.For optimal performance, data sets that reside on tapes thatcan be read only in a single direction, such as 3480s, should have two units allocated.Ifthe data set is on a tape that supports bidirectional processing, a single unit is sufficient.In all cases DEFER mounting must be specified.

also that each example includes an alternative UNIT specification:UNIT=(xxxxx1,y,DEFER).This specification applies if special esoteric names are avail-able.The xxxxx1 is a special esoteric unit name established especially for PARASORT.These esoteric names may have been created at your site for use with PARASORT. Con-tact the systems programmer responsible for SyncSort installation to determine if theyare available.For information on how to select a speciahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1al esoteric name, see “SpecialChannel Separated Esoteric Names” on page 10.7

1

consists of a single multi-volume cataloged data set.//SORTIN DD DSN=INPUT.FILE,DISP=(OLD,KEEP),

// UNIT=(,y,DEFER)

if a special esoteric name is available

// UNIT=(xxxxx1,y,DEFER)

.Sample SORTIN DD Statement

.4 Programmer'sGuide

Example 2

consists of a single multi-volume uncataloged data set.//SORTIN DD DSN=INPUT.FILE,DISP=(OLD,KEEP),

// UNIT=(3480,y,DEFER),VOL=SER=(VOL001,VOL002,...,VOL00N)

if special esoteric name is available

// UNIT=(xxxxx1,y,DEFER),VOL=SER=(VOL001,VOL002,...,VOL00N)

.Sample SORTIN DD Statement

example presumes the file is standard label and the first file is on VOL001.For uncataloged data sets, the unit and volser list must be specified.

3

consists of ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a concatenation of single and multi-volume uncataloged data sets.//SORTIN DD DSN=INPUT.FILE1,DISP=(OLD,KEEP),

// UNIT=(3480,y,DEFER),VOL=SER=(VOL001,VOL002,VOL003)

if special esoteric names are available

// UNIT=(xxxxx1,y,DEFER),VOL=SER=(VOL001,VOL002,VOL003)

// DDDSN=INPUT.FILE2,DISP=(OLD,KEEP),

// UNIT=AFF=SORTIN,VOL=SER=(VOL101,VOL102)

// DDDSN=INPUT.FILE3,DISP=(OLD,KEEP),

// UNIT=AFF=SORTIN,VOL=SER=(VOL201)

.Sample SORTIN DD Statement

is also possible to include a DD DUMMY allocation in the SORTIN concatenation.Thisis necessary when modifying production JCL that is a prototype for the maximum numberof possible concatenated input files. If a particular execution uses less than the maximumnumber, place the DD DUMMY specification at the appropriate point.This specificationshould contain a DCB specification that matches that of the first SORTIN data set.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarDD Statements

SORTPARn DD statements define units that will be used to perform the parallelreading of the input file. Up to four SORTPARn DD statements may be provided, with aminimum of two required.The number of SORTPARn DD statements that you providemay be limited by the tape channel capacity at your installation.See “Special ChannelSeparated Esoteric Names” on page 10.7 for information on how to determine if yourchoice is limited.

10. PARASORT10.5

The n in the SORTPARn is replaced with numbers 1 through 4.The numbers must startat 1 and be numbered consecutively.

required SORTPAR1 must be coded in one of the following two ways, depending onwhether the SORTIN data set is cataloged or not.

If the SORTINDD is defined as a single cataloged data set or as a series of con-

data sets where the first data set of the concatenation is cataloged, thenthe Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aORTPAR1 DD must be coded as follows://SORTPAR1 DDDSN=*.SORTIN,DISP=OLD,

// UNIT=AFF=SORTIN

.

Sample SORTPAR1 DD StatementIf the SORTIN DD is defined as a single non-cataloged data set or as a series of

data sets where the first data set of the concatenation is noncataloged,then the SORTPAR1 DD must be coded as follows://SORTPAR1 DDDSN=*.SORTIN,DISP=OLD,UNIT=AFF=SORTIN,

// VOL=SER=(VOL001,VOL002,...,VOL00n)

.Sample SORTPAR1 DD Statement

the VOL=SER list contains the identical volumes specified on the SORTIN DDspecification.If the SORTIN DD is a series of concatenations, the VOL=SER list isthe volumes that comprise the first data set in the concatenation.

remaining SORTPARnn DDs are coded as shown on the following prototypeSORTPARnn DD statement://SORTPARn DDDSN=*.SORTIN,DISP=(,KEEP,KEEP),

// VOL=PRIVATE,UNIT=(xxxx,y,DEFER)

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aror if special esoteric names are available

// VOL=PRIVATE,UNIT=(xxxxxn,y,DEFER)

.Prototype SORTPARn DD Statement

xxxx is a unit type or generic name compatible with the device associated withSORTIN. If special channel separated esoteric names have been made available, see“Special Channel Separated Esoteric Names” on page 10.7.

y is either 1 or 2 and indicates the number of units to be allocated for these devices.For optimal performance, data sets that reside on tapes that can be read only in a singledirection, such as 3480s, should have two units allocated.If the data set is on a tape that

.6 Programmer'sGuide

supports bidirectional processing, a single unit is sufficient.In all cases DEFER mount-ing must be specified.

number of SORTPARn data sets to allocate depends on several factors:

The total number of volumes to be read from SORTIN and its concahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atenations.

is no need to allocate more SORTPARn data sets than total volumes inthe SORTIN file.Note that if more SORTPARn data sets are allocated thanthere are volumes, the excess SORTPARn data sets will be deallocated atPARASORT's initiation.

degree of performance improvement desired.

, two SORTPARn datasets will provide up to 20% elapsed time im-provement; three, up to 25%; and four, up to 33%.

degree of channel contention, which may reduce the number of SORTPARn DDstatements used.

use of special esoteric unit names will ensure that this contention is elimi-nated, but your choice for the number of SORTPARn DD statements may belimited.

.

constraints may limit the number available to a particular job.

Channel Separated Esoteric Names

optimal PARASORT performance, SyncSort must be able to read each SORThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPARninput DD simultaneously, with no channel contention.To ensure this, your system pro-gramming staff may have defined special esoteric unit names for use with PARASORT.Before creating a PARASORT application, you should contact your system programmerto verify that this work has been done and that the special names are available for use.Note, however, that even if the work has been done, certain categories may be unavailabledue to limited channel capacity.

use special esoteric names, do the following:

.Decide whether you would like to specify 4-way (up to SORTPAR4), 3-way (up to

) or 2-way (up to SORTPAR2) input.

the table of special esoteric names provided by your systems programmer, find thename that corresponds to the tape type of the SORTIN data sets.

following is a sample table of special esoteric names.This table is for illustrationonly; the names at your site may be diffehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arent.2.

10. PARASORT10.7

-WAY

-WAY

-WAY

3480/90 3490E3590|----------|----------|----------|----------|| PAR241 | PAR441 | PARE41 |NOT|| PAR242 | PAR442 | PARE42 |POSSIBLE|| PAR243 | PAR443 | PARE43 ||| PAR244 | PAR444 | PARE44 |||----------|----------|----------|----------|| PAR231 | PAR431 | PARE31 |NOT|| PAR232 | PAR432 | PARE32 |POSSIBLE|| PAR233 | PAR433 | PARE33 |||----------|----------|----------|----------|| PAR221 | PAR421 | PARE21 | PAR921 || PAR222 | PAR422 | PARE22 | PAR922 ||----------|----------|----------|----------|

.

.Sample Esoteric Unit Name TableUse the name from the table at your site for your SORTIN and SORTPARn names.

following example JCL is for input from 3480 cartridges with at least 4 volumes://SORTIN DDDSN=....,DISP=(OLD,KEEP),UNIT=(PAR441,2,DEFER)

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar//SORTPAR1 DD DSN=*.SORTIN,DISP=OLD,

// UNIT=AFF=SORTIN

//SORTPAR2 DD DSN=*.SORTIN,DISP=(,KEEP,KEEP),

// VOL=PRIVATE,UNIT=(PAR442,2,DEFER)

//SORTPAR3 DD DSN=*.SORTIN,DISP=(,KEEP,KEEP),

// VOL=PRIVATE,UNIT=(PAR443,2,DEFER)

//SORTPAR4 DD DSN=*.SORTIN,DISP=(,KEEP,KEEP),

// VOL=PRIVATE,UNIT=(PAR444,2,DEFER)

Considerations

amount of sortwork space required is the same as if the application were run as aconventional sort.What should be modified, if sortworks are provided via JCL ratherthan DYNALLOC, is the number of SORTWKnn DD statements. Try to provide a totalnumber of SORTWKnn DDs that is two to three times the number of SORTPARns spec-ified. This would typically require an adjustment in primary and secondary spaceamounts so that the total space allocated is similar to that of the original application.This subdivision of SORTWORK space will provide an opporthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aunity for additional channelpath availability. This parallelism in SORTWORK channel paths is also a key to im-proving sort elapsed time performance.

.8 Programmer'sGuide

Operations Notes

the SORTIN tape volumes will be read in an order and on a SORTPARn tape unitlocation determined by the PARASORT logic, it is possible to receive messages on theconsole log that indicate out of sequence processing of the volumes of the SORTIN dataset.Messages such as the following may be generated:

I ... SORTPARn READ - NOT FIRST VOLUME OF DATA SET

I ... SORTPARn ANOTHER VOLUME EXPECTED

messages can be disregarded since this type of processing is deliberate withPARASORT.

10. PARASORT10.9

10.10 Programmer'sGuide

Chapter 11. Tape Sort

to Use Tape Sort

, Tape Sort has been used where there is insufficient diskhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a space for sortwork. Currently, MAXSORT is the recommended sorting technique for large applications:

(1) MAXSORT's disk SORTWK allocations can be defined independently of SORTIN size;

(2) when a MAXSORT job is canceled for higher priority jobs, all previously produced datasets can be used without resorting; (3) all Disk Sort features and performance improve-ments are available with MAXSORT; (4) significantly less tape drive time is required; and

(5) the job can be executed in segments to facilitate production scheduling.

Reserved to Disk Sort

PARMs are reserved for sorts with SORTWK assigned to disk:BALANCE, BMSG,CMP=CPD/CLC, COMMAREA/NOCOMMAREA, CPU, DEBUG, DYNALLOC, ELAP,E15/E35=COB, FILSZ=n, HBSI, HBSO, INCOR=ON/OFF, IO, LIST/NOLIST, NOIOERR,L6/L7=n, PRINT121, NORC16, RELEASE=ON/OFF, RESET, RLSOUT, SDB=xxx,SECOND=ON/OFF, SKIPREC=n, STOPAFT=n, VLTEST=n/0, VLTESI=n/0, and allMAXSORThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a PARMs.

Sort will not validate decimal control fields, permit exits written in COBOL, C, orREXX, check the size of the input file after input processing, run incore, abend withouta dump, optimize with HISTOGRM, issue the STIMER macro, adjust the message dataset's DCB, release unused SORTWK or SORTOUT space, accept VSAM input, or stopprocessing after a specified number of records. Control statements and header line(s) ap-

11. Tape Sort11.1

pear with SYSOUT if Tape Sort is initiated through job control language; invoked TapeSorts do not list sort control statements.

Tape Sorts may only use the 24-bit addressing mode.

control statements are reserved for sorts with SORTWK assigned to disk: MERGE,INCLUDE/OMIT, INREC, OPTION, OUTREC, OUTFIL, SUM, and ALTSEQ. In addi-tion, the SORT statement does not permit COPY, DYNALLOC or FILSZ=n.

Statement

Tape Sorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a EXEC statement differs from that for a Disk Sort in that thePGM=SYNCSORT coding cannot be used.  //stepnameEXEC   PGM=SORT PGM=IERRCO00 PGM=IGHRCO00  PGM=ICEMAN     [,PARM='...' ]

.Tape Sort EXEC Statement Format

addition, the set of PARMs is restricted to the following list.      PARM='

BALN  OSCL  POLY    , CORE  SIZE       , CORE  SIZE   =   n nK MAX MAX-n MAX-nK n nK( MAX MAX-n MAX-nK        )                  ,FLAG(I)  ,FLAG(U)  ,NOFLAG   ,RC16=ABE '       ,EQUALS    ,DIAG          ,FILSZ=En      ,IOERR=ABE  ,MSGDD= SYSOUT      xxxxxxxx

.Tape Sort PARM Parameter Format

usual, the PARM list is enclosed in single quotes.

.2 Programmer'sGuide

The BALN/OSCL/POLY PARM option is effective only with Tape Sort, where it specifiesthe balanced (BALN), oscillating (OSCL) or polyphase (POLY) sorting technique. It isrecommended that this PARM valhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aue be omitted, permitting the sort to choose the tech-nique best suited to the application.

Statements

Sort's DD statements are summarized in the table below. They differ from DiskSort's only in the additional requirement of a SORTLIB statement. SORTWKnn DDstatements are required--Tape Sort is initiated by assigning these to tape. $ORTPARMis restricted to one 80-byte card image, which can include only PARMs.

Sort DD Statements

//$ORTPARM

//SYSIN

//SYSOUT

//SORTWKnn

//SORTLIB

//SORTIN DDDDDDDDDDDDUsed to override PARM information. Restricted to one 80-bytecard image.Control card input data set. Required unless the invokingprogram supplies the address of a 24-bit parameter list.Message data set.Required. Assigned to tape.Required. Refers to tape sort library.Sort input data set. Required unless there is an E15.Ignored

the invoking program supplies ahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an inline E15 exit routine;

if the MODS statement activates an E15 exit routine.

output data set. Required unless there is an E35.Ig-

if the invoking program supplies an inline E35 exit

; optional if the MODS statement activates an E35 exit

.

data set. Required if Checkpoint-Restart is used.

if user exits are in SYSIN and if user exits are to

linkage-edited at execution time.//SORTOUT DD//SORTCKPT //SORTMODS //SYSLIN

//SYSLMOD

//SYSUT1

//SYSPRINT

//ddname DDDDDDDDDDDDDDLibrary definition of user exits. Required unless exits are in

.

.Tape Sort DD StatementsChapter 11. Tape Sort11.3

SORTLIB DD Statement

SORTLIB DD statement is required to reference the special tape sort program.//SORTLIB DDDSN=SYNCTAPE,DISP=SHR

.Sample SORTLIB DD Sthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aatement

this example, the tape sort modules are in a partitioned data set called SYNCTAPE.The modules will be used as needed by the Tape Sort control program which was givencontrol by the operating system.

DD Statement

Sort is initiated by the use of tape devices for intermediate storage. Tape Sort re-quires a minimum of three SORTWKnn DD statements, numbered consecutively from 01.There may be as many as thirty-two sort work files, making 32 the largest possible nnvalue.

Sort uses 2400 and 3400 series tape units, including the 3480, 3490 and 3590 car-tridge systems, with densities of 800 BPI, 1600 BPI, and 6250 BPI.Each reel of tapemust be a full-size 2400-foot reel. It is possible to mix different densities or device typeswithin the same sort, but SyncSort will use the lowest density to calculate the capacityof each SORTWK volume. If 3480 or 3490 IDRC tape drives are used,DCB=TRTCNhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a=NOCOMP must be in effect.

Figure207, the xxxx in the UNIT parameter represents the installation--specific namechosen to define a tape device.  //SORTWK01 DD  UNIT= 2400 3400 3480 3590 xxxx

.SORTWKnn DD Statement Format for Tape Sorts

Tape SORTWK Requirements

number of files needed for intermediate storage varies with the size of the input andthe sorting technique used (BALN, OSCL or POLY).The table below indicates the min-imum required for each of the three sorting techniques. This minimum figure is not therecommended number to use--allow more than the minimum number of drives to achievesorting efficiency.

.4 Programmer'sGuide

Sorting

. InputTapes15MinimumNo. TapeDrives ForSORTWKs(no. inputvolumes

) or four,

larger.

times

(no. of input

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ane).

.MaximumNo. TapesForSORTWKs17Note that...(1) An exact or a closely estimatedSIZE on the SORT statement is neces-sary.(2) SORTIN and SORTWK tapes maynot be mounted on the same drive.(1) An exact or a closely estimatedSIZE is recommended.(2) Provide a generous amount ofmemory.POLY is always used, whether speci-

or not, when only 3 SORTWK tape

are available. This technique is

recommended unless necessary.BALN1532POLY117

.Tape Sort Requirements$ORTPARM DD Statement

used in conjunction with Tape Sort, $ORTPARM can pass only PARM-coded in-formation, and then only by way of a single 80-byte card image. $ORTPARM cannot beused to override control statements for Tape Sort.

following example changes three PARM options.

//$ORTPARM DD*

=128K,EQUALS,FILSZ=E15000

.Sample Tape Sort $ORTPARM Data Set

Tape Sohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art

factors are crucial to Tape Sort efficiency: a generous amount of intermediatestorage, a closely estimated input size value on the SORT or EXEC statement, and thefreedom to select the best sorting technique (BALN, OSCL or POLY) based on the natureof the application and conditions at execution time. Accordingly, the number of SORTWKdata sets should be in excess of those suggested in the chart above, the

11. Tape Sort11.5

BALN/OSCL/POLY PARM should be omitted and an accurate SIZE or FILSZ estimateshould be provided.

.6 Programmer'sGuide

Control Statements

Sort supports only four control statements: SORT, RECORD, MODS and END. Ofthese four, only MODS and END are supported in their full Disk Sort version, and MODSis available only for JCL-initiated executions.  FIELDS=(p1,l1,f1,o1,p2,l2,f2,o2,...,p64,l64,f64,o64)SORT    FIELDS=(p1,l1,o1,p2,l2,o2,...,p64,l64,o64),FORMhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aAT=f

n      ,SIZE=  En     ,FILSZ=En   ,SKIPREC=n

,EQUALS  ,CKPT      ,CHKPT

.SORT Control Statement Format for Tape Sort

F RECORD TYPE=  V ,LENGTH=(l1,l2,l3,l4,l5)

.Tape Sort RECORD Control Statement Format

,N    ,N  MODS exit-name1=(r1,b1 [,d1]  ,S  ) ...,exit-name16=(r16,b16[,d16]  ,S  )

.

.MODS Control Statement FormatEND Control Statement Format

11. Tape Sort11.7

Exit Programs

the exception of the merge input exit E32, all of the exits available for Disk Sort aresupported for a JCL-initiated Tape Sort.When invoked, however, only E15 and E35 exitsare available; these must be coded as subroutines of the calling program. The MODSstatement is not supported for an invoked Tape Sort.

Tape Sort Through JCL/Control Streams//TAPESORT

//STEPThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

//SORTLIB

//MODLIB

//SYSOUT

//SORTIN

//

//

//

//SORTOUT

//

//SORTWK01

//SORTWK02

//SORTWK03

//SORTWK04

//SORTWK05

//SORTWK06

//SORTWK07

//SORTWK08

//SYSIN

*

/*JOBEXECDDDD DD DD 123456PGM=SORTDSN=TAPESORT.RESI.DENCE,DISP=SHRDSN=EXIT.E15,DISP=SHRSYSOUT=ADSN=INTAPE,UNIT=3480,VOL=SER=385678,DISP=(OLD,KEEP),DCB=(LRECL=100,RECFM=FB,BLKSIZE=900)DDDSN=OUT.TAPE,VOL=SER=783456,UNIT=3480,DISP=(NEW,KEEP)DDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDDUNIT=TAPEDD*FIELDS=(1,15,CH,A,16,8,BI,D),EQUALS,SIZE=E20000TYPE=F,LENGTH=100E15=(E15,550,MODLIB,N)END TAPE SORTMAY ACCOUNTS PROCESSED7891011121314

.

.

.Sample JCL/Control StreamThe JOB statement gives TAPESORT as the name of the job.The EXEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aC statement identifies SORT as the program to be executed.

.8 Programmer'sGuide

3.The required SORTLIB DD statement instructs the system to look for the Tape Sort

modules in the SORTLIB library under the data set nameTAPESORT.RESI.DENCE. The DISP shows that this library may be shared.

MODLIB DD statement defines the partitioned data set in which the exit routineresides. (Note that MODLIB is referenced in the MODS control statement.) The dataset name of the exit library is EXIT.E15, and the DISP shows that the library maybe shared.

SYSOUT DD statement assigns the SyncSort messages to the output device as-sociated with SYSOUT class A.

SORTIN DD statement gives INTAPE as the input data set name, and specifiesa 3480 tape unit with the volume serial number 385678. The DISP shows that thedata set is already in existence.

DCB parameter shows in LRECL of 100 bythttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aes, a fixed blocked RECFM, and a900 byte BLKSIZE.4.5.6.

.The SORTOUT DD statement gives OUT.TAPE as the output data set name, and

a 3480 tape unit with the volume serial number 783456. The DISP param-eter shows that this data set is not in existence yet. The DCB parameter for theSORTOUT data set defaults to that of SORTIN.

eight SORTWK DD statements indicate that 8 tapes are to be used for interme-diate storage.

SYSIN DD * statement marks the beginning of the system input stream thatincludes the program control statements.8.9.

.The SORT control statement shows that two control fields are to be sorted on. The

begins on byte 1 of the record, is 15 bytes long, has character data, and is to besorted in ascending order.The second begins on byte 16 of the record, is 8 bytes long,contains binary data, and is to be sorted in decending order. EQUALS requests thatrecords wihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ath equal control fields leave the sort in the same order in which they camein. The SIZE parameter shows that the number of records in the input data set isestimated at 20,000.

.The RECORD control statement shows that fixed length records are being sorted. The

parameter shows 100 byte records at input, during the sort, and at outputtime.

.The MODS control statement gives E15 as the exit-type. The name of the exit routine

also E15. It will take 550 bytes in main storage, and resides in a library definedon the MODLIB DD statement. (See the MODLIB DD statement.) The N indicatesthat link-editing has already been performed.

.The END control statement marks the end of the control statements. A comment is

.

11. Tape Sort11.9

14.This is a comment card.

.The delimiter statement marks the end of the SYSIN input stream.

Tape Sort frohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1am a Program

initiating Tape Sort from a program, only certain parameters from the parameterlist are processed The X'02' (MODS), X'04' (merge input files), X'05' (DEBUG), X'06'(ALTSEQ), X'07' (SUM), X'08' (INCLUDE/OMIT), X'09' (OUTREC), X'0A' (INREC), X'0B'(OUTFIL), X'F6' (ALTSEQ translation table), and X'F7' (User address constant) parame-ters are ignored. When invoked, Tape Sort supports only the E15 and E35 exits, whichmust be coded in line with the invoking program.

.10 Programmer'sGuide

ADDRESS OF POINTERPOINTER(Fullword)X'80'Address of Parmlist Byte Count Fullword Boundary↓

1Byte 2   ↓Byte 3Byte 4

of bytes in following list

'00'

in

'00'X'00'X'00'

'00'

'00'

'00'

'01'

'03'

'05'Beginning address of SORT statementEnding address of SORT statementBeginning addresshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a of RECORD statementEnding address of RECORD statementAddress of E15 exit routine (zeros if none)Address of E35 exit routine (zeros if none)Main storage valueReserved main storage valueBeginning address of message DD name to replaceSYSOUTBeginning address of DEBUG statement (not processed)

address of DEBUG statement

'FD'

'FE'

'FF'IMS flagPointer to STAE work area (may code zeros if none)Message options (code in EBCDIC)

option (code in EBCDIC)

OSCL or PLY (code in EBCDIC)

, PEER or LIST (not processed)

name prefix to replace SORT in JCL (code in EBCDIC)

.Tape Sort Parameter ListChapter 11. Tape Sort11.11

://www.wendangwang.comLINKLTRBNZ Bhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCNOPDCDCDSDCDCDCDCDCDC DC http://www.wendangwang.comINGDS...DS...BRDS...

,PTRWORDLoad address of pointer to parameter listEP=SORTInitiate tape sort15,15Test tape sort return codeSORTERR BranchonerrorconditionSORTOKBranch to normal processing0,4Fullword alignment for pointerX'80'Indicates pointer to parameter listAL3(PARMS) Address of parameter listHUnused first two bytes of first parameterY(28)Byte count of remaining parametersA(SORTBEG) Beginning address of sort statementA(SORTEND) Ending address of sort statementA(RECBEG)Beginning address of record statementA(RECEND)Ending address of record statementA(E15) AddressofE15exitroutineA(E35) AddressofE35exitroutineC'DIAG'Turns on IOERR=ABE and RC16=ABE optionsC'SORTFIELDS=(19,6,PD,A,5,10,CH,A),EQUALS' Sort image beginsC' 'Sort image endsC'RECORD TYPE=V,LENGTH=(104,,,64,84)' Record image beginsC' 'Record image ends*,15Using 15 as base register0HExit E15 has full responsibilityhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a for sort input*,150HUsing 15 as base registerExit E35 has full responsibility for sort output 0HError routine for unsuccessful sort140HReturn to invoking programNormal processing for successful sort14Return to invoking program

.Sample Invoked Tape Sort

this example, Tape Sort's input file is provided by the in-line E15 exit routine. Sincethis causes the sort to ignore a SORTIN DD statement, therequired RECORD controlstatement must include the LENGTH parameter. The RECORD statement specifies thatthe records to be sorted are variable in length, ranging from 64 to 104 bytes long at sort

.12 Programmer'sGuide

time, that the most frequent input record length is 84, and that the maximal length of104 is not changed by the E35 exit routine; all length values include theRecord De-scriptor Word's 4 bytes. The records are sorted in ascending numeric order by the packeddecimal data in the 15th - 20thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ah data bytes in the record. Records with equal numericvalues in this field are further sorted by the character data in their first 10 data bytes,in ascending order. Records with equal control keys are passed to the E35 exit routine inthe same order as they were generated by the E15 exit routine (the EQUALS parameter).The DIAG option is also set.

11. Tape Sort11.13

11.14 Programmer'sGuide

Chapter 12. Performance Considerations

Sort? MAXSORT? PARASORT? Tape Sort?

Sort provides the current, established sorting technique, suitable for most sort/merge

.Intermediate storage is allocated on disk devices and the sort size is limited

the allocated disk space plus secondary extents automatically obtained by the sort.

, SyncSort's maximum capacity sorting technique, is not limited by disk space

.MAXSORT determines how much dahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ata can be sorted using the available disk

space and divides SORTIN into SORTWK-manageable segments; the sorted seg-

are stored on tape, disk or MSS for a later, automatic merge.MAXSORT makes

the Disk Sort operational optimizing features and modern programming options

to large sorts, and additionally provides an enhanced breakpoint/restart capa-

for greater scheduling flexibility--the user can stop MAXSORT processing at se-

intervals without loss of sorted output.

improves elapsed time performance for sorts whose input is read from a

-volume tape data set and/or concatenated tape data sets.The performance im-

from PARASORT is a result of processing the SORTIN input volumes in a

fashion.PARASORT requires two to eight times the current number of tape

, depending upon resource availabhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aility and the degree of improvement desired.

automatically manages the tape units and minimizes the use of the tape

resources by deallocating excess tape drives during initialization and releasing all

extra units at the end of the sort input phase.

definition, Tape Sort uses tape for intermediate storage.This inhibits such state-of-

-art sorting techniques as sophisticated disk I/O methods, high order merges, and

12. Performance Considerations12.1

modern parameter capabilities.For these reasons, MAXSORT performance is far supe-

to that of Tape Sort.MAXSORT is therefore the preferred method of handling all

previously routed to Tape Sort.

convert a Tape Sort execution to MAXSORT, these changes must be made:

Use the $ORTPARM DD statement to pass the MAXSORT PARM or (if the sort is

throuhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1agh JCL) add PARM='MAXSORT' to the EXEC statement.

SORTWK files to disk (SORTWK requirements are independent of SORTIN

).

a SORTBKPT DD statement.

2 or more SORTOUnn DD statements for the intermediate output and, if

are allocated to tape (as is usual), a SORTOU00 DD statement.

exits are included or the sort is invoked, supply a SORTCKPT DD statment in case

should be necessary.

(Optional.)Remove the SORTLIB DD statement.

that it may be necessary to supply additional memory in order to execute

.

Sorts vs. Program-Invoked Sorts

SyncSort is initiated from a COBOL program, the calling program handles I/O,

in core, and generally retards sort execution.SyncSort will yield maximum

through proper synchronization of all data whenever it has control of the://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarprocess, i.e., whenever // EXEC PGM= SYNCSORT is used.

the point of view of performance, the JCL-initiated sort execution has the advan-

.Whenever possible, tasks incidental to the sort/merge/copy process should be han-

via SyncSort control statements.Where this is not possible, the JCL/control stream

be supplemented with user-written exit routines.Ideally, the exit routines exist

load modules, so that they do not require link-editing every time the job is run.

permits exit routines to be written in COBOL, C, FORTRAN, REXX, or As-

language.

you must invoke the sort from a COBOL program, you may improve sort performance

passing an accurate FILSZ=n/En parameter via $ORTPARM.

Statement Issues

control statements can be used to eliminate records from the input file

(INCLUDE/OMIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aT), summarize and/or eliminate equal-keyed records (SUM), reformat

(INREC/OUTREC), set up multiple output files (OUTFIL) or write formatted re-

(OUTFIL statement with HEADER, TRAILER, SECTIONS and OUTFIL parame-

.2 Programmer'sGuide

ters.These control statements provide a high performance alternative to the use of exits

invoking programs.The tasks they address are those which are most frequently ex-

and/or improve sort performance.Since sort throughput is in part a function of

number of bytes that are to be manipulated, considerable performance savings can

from using the INCLUDE/OMIT statement to eliminate irrelevant records;

/OMIT affects the data set prior to sorting/merging/copying.The SKIPREC and

parameters are recommended for test runs of sorting applications for the same

.When the file biashttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a is high enough for a significant number of records to be sum-

early in the sort, SUM will also provide performance gains if the XSUM option

not also been selected.When reformatting records, it is desirable to minimize the

of data that must pass through the sort process.Other things being equal,

should be used to shorten records, OUTREC to lengthen them.

Efficient Use of PARMs

are four programming PARMs that may have a significant effect on sort perform-

: CMP, EQUALS, STOPAFT and SKIPREC.

CMP PARM specifies the kind of compare operation to be used for sort/merge control

up to 16 bytes long, bearing the format code PD or ZD.When CMP=CPD, the de-

, is used, ZD fields are PACK'ed and then compared.Invalid PD data may cause a

0C7 abend and program termination.The integrity of fields labelled &quothttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a;ZD&quot; is only

when they contain valid ZD data.The delivered default of the VLTEST

supports CMP=CPD, as do certain other VLTEST PARM values.Whenever pos-

, set CMP= CPD for better sort performance.

alternative, CMP=CLC, is a more costly option--it forces the sort to extract poten-

invalid PD and ZD fields and do a certain amount of data manipulation to obtain

sign comparisons.

EQUALS PARM instructs the sort/merge to preserve the order of equal-keyed re-

.EQUALS will have a slight but generally significant impact on sort performance.

making EQUALS available on an individual sort basis, SyncSort makes this pro-

option available where it is needed, without imposing it on the installation's

routine jobs.For sort efficiency, use EQUALS only where the preservation of the

order of equhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aal-keyed records is important.

user interested in sort performance will specify the STOPAFT PARM in test runs of

sort.With STOPAFT=n, only the first n records of the input file will be sorted.By

the number of records to be processed, STOPAFT improves sort performance.

additional tests are necessary, the SKIPREC PARM can be used together with

to select a different subset of the SORTIN data set.

12. Performance Considerations12.3

Optimizing System Resources

efficiency of sort processing is measured in terms of three categories of system re-

, which are CPU time, elapsed time and I/O activity. Ordinarily, when SyncSort

a sort, it seeks to balance these categories in a way that yields the best overall

performance. It is possible, however, to define a particular system resource as more

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aant than others in the performance of a job. This can be done through SyncSort's

Storage Management (DSM) facility, which makes available four optimization

for sort processing.These are BALANCE, CPU, ELAP and IO. BALANCE is the

optimization mode which provides the best overall balance between CPU time,

elapsed time and I/O activity to SORTIN, SORTOUT and SORTWK.If CPU time is

the highest priority, SyncSort will minimize this resource at the expense of elapsed

and I/O activity. Selecting ELAP as the optimization mode will cause SyncSort to

the elapsed (wall clock) time of each sort, usually at some expense of the sort's

time. Likewise, if IO is selected as the optimization mode, SyncSort will minimize

I/O activity (EXCPs) performed by the sorts.

CORE

following examples illustrate the most cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ammon types of alternative codings for the

PARM:

=MAX-30K

=500K

=MAX

the perspective of memory management, there are three types of sort executions,

three different approaches to CORE coding: invoked sorts, JCL sorts with exit

, and JCL sorts without exit routines.

the first case, where for example, a COBOL program calls SyncSort via the SORT verb,

sort and the invoking program (including its Input Procedure and Output Procedure)

all in memory at the same time.The only dynamic aspect to memory management

this case is the acquisition of memory for the buffers of any files opened by the Input

Output Procedures; it is only when a file is opened that the memory for the file's

is obtained.Therefore, all data sets required during the sort should, if possible,

opened before ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anvoking the sort.

coding of the CORE parameter must make allowances for the Input and Output

' file buffers by reserving enough memory for the greater of the two procedures'

.If, for example, the Input Procedure's files require 50K and the Output

's files require 100K, SyncSort should be instructed to set aside 100K for their

; code CORE=MAX-100K.If CORE=MAX is coded, it is likely that no memory will be

for buffers when the Input or Output Procedure attempts to open a file, result-

in an ABEND80A message.If CORE is coded with a constant value such as

=756K, there is still thepossibility of an ABEND80A message since the constant

.4 Programmer'sGuide

value requested (in this case, 756K) may account for all the memory available, again

no memory for the buffers.

CORE=MAX-100K, the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aprecise amount of memory used by the sort depends both

the amount of memory that is available and on the maximum value set at sort instal-

time (the site maximum).Since this form of the parameter ensures that 100K of

total memory available to this job will be set aside for the buffers, CORE=MAX-100K

not produce an ABEND80A message.Note that MAX-value must be greater than the

memory requirement for SyncSort execution.

table below illustrates the relationship between the site maximum and the available

for an invoked sort requiring 100K bytes worth of buffers for the Input and

Procedures.In reviewing the table, note that the site maximum sets an absolute

on the amount of memory that can be used by the sort; even if additional memory

available, it is not available to the sort.This additional memory would, howevehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar, be

to the Input or Output Procedure for file buffers, accounting for some of the

sort terminations indicated.Since the programmer has no way of knowing

these conditions will hold at execution time, CORE=MAX-100K remains the

method of setting memory for an invoked sort with 100K bytes worth of buffers.

COBOL programmer has the option of setting CORE by means of the

-CORE-SIZE special register.In order to set memory aside for the buffers, the in-

program places a negative value into the special register prior to sort execution;

=MAX-100K is equivalent to MOVE-102400 TO SORT-CORE-SIZE.Under VS

II or COBOL/370, CORE can be set by submitting the CORE=MAX-nK PARM

the $ORTPARM data set.

Maxi-

=Memoryused by

Sort

K

K

K://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

K

K

K

K

K

K

KAvailablefor 100KBufferSpace00100K100K100K0100K100K100K100KProbable Sort ReturnCode1024K1024K1024K1024K512K1024K1024K512K512K1024K

.1024K512K2048K900K2048K756K512K512K1024K360KMAXMAXMAX756K756K756KMAX-100KMAX-100KMAX-100KMAX-100KS80A - No core for buffersS80A - No core for buffers000S80A - No core for buffers0000 - Inefficient sortIllustration: CORE Alternatives for Invoked Sort with 100K Buffer SpaceChapter 12. Performance Considerations12.5

When exits are included, the optimal coding of the CORE parameter depends on the

value in the MODS control statement.As in the case of the COBOL

/Output Procedure, coding CORE=MAX-100K will set aside 100K bytes for buffers.

the MODS statement's memory value included sufficient buffer space, code

=MAX; coding anything but CORE=MAX nullifies the MOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aDS memory value(s).

, the site maximum prevents the sort from appropriating too much memory.When

exit program is not referenced in a MODS statement (e.g., when an E15/E35 exit

is coded in line with an invoking Assembler program) or the MODS memory value

only for the program's code, memory must be reserved for the buffers of any files

be opened.An Assembler program's in-line E15/E35 exit routine is equivalent to a

Input/Output Procedure.

JCL sorts without exit routines, it is not necessary to code any core parameter.

will use as much of the site maximum as is available at the time of execution.

, if the site maximum is set to 1024K and 2048K bytes are available, SyncSort will

1024K.

Incore Sort

incore or turnaround sort is only possible when the INCORE PARM has the value ON.

(This ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as the delivered default for this PARM.)

there is sufficient memory, INCORE=ON permits the standard Disk Sort to

all the input data within its memory area, without writing to any of the work data

that may have been provided. Sufficient memory, as discussed here, means that

's memory area/address space is large enough to hold the SyncSort program, all

the input data, SORTIN or SORTOUT buffers (whichever are larger) and, if work data

are allocated, SORTWKnn buffers.

incore sort is not available to Disk Sorts taking checkpoints, usingSUM, OUTREC,

, an E14 or E16 exit routine, or producing VSAM output.INCORE=ON is ig-

by Tape Sort, MAXSORT and PARASORT.

Can a Sort Run Entirely in Main Storage (No SORTWK Needed)?

Incore Sort is possible when all of the data that is to be sorted can be contained in

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1armain storage. For most simple applications:D   12

= Core available to SyncSort.

= 200K

= The greatest of: 2 X SORTIN block size, 2 X SORTOUT block size, and 15% of A.

= Average record length of data being sorted.

.6 Programmer'sGuide

Note:SORTWK data sets are required in order to use SUM, OUTREC, OUTFIL, a VSAM

data set, checkpoint/restart, an E14 or E16 exit routine, MAXSORT or

.

Space Considerations

Disk Space Allocations

the operational features SECOND and RELEASE turned ON (this is the delivered

), SyncSort automatically supplements and releases any disk space the user allo-

for intermediate storage, making the allocation of the correct amount of SORTWK

an automatic, sort-controlled process.For general sorting purposes, the user need

be concerned with precihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ase SORTWK space allocations.However, allocating SORTWK

in cylinders, rather than blocks or tracks, will usually yield optimal performance.

WER124I is provided in some applications in order to permit the user who is

in a finely tuned sort execution to improve intermediate storage allocation for

runs. Routinely overallocating SORTWK, relying on RELEASE=ON, will delay sort

execution until all the space requested (including the excess space) is available, and

waste this excess space until its released at the end of Phase 1. Routinely underal-

by a large amount assumes that the needed storage will always be physically

. If, for some reason, the required storage cannot be obtained on any volume

for sort work areas, SyncSort will terminate with a SORT CAPACITY EX-

error.

sort is considehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ared to finely tuned when WER124I reports an overallocation factor be-

1.00 and 1.50.

Impact of Disk Space on the Work Data Sets on SyncSort

's work data set disk space management is automated to a very high degree. It

:

Automatically correct the underallocation of disk space by obtaining secondary allo-

of disk space, as needed.This prevents costly SORT CAPACITY EXCEEDED

.

release excess disk space at the completion of Phase 1. The space im-

becomes available for allocations to other jobs.

allocate work data sets through the MVS DYNALLOC capability.

can improve the efficiency of disk space usage by allocating optimally at the outset.

12. Performance Considerations12.7

Disk Sort Intermediate Storage Calculation Formulas C

:

= Numbhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aer of records to be sorted.

= Average record length of data being sorted.

= Track capacity of the work device:

TYPE

TRACK CAPACITY IN BYTES19,06936,00047,47656,66446,456

disk storage space in cylinders rather than tracks will improve the perform-

of SyncSort. When converting tracks to cylinders, round the number of cylinders up

the higher number. For example, if 9.5 cylinders are needed, allocate 10 cylinders.Tape Sort Intermediate Storage Calculation Formulas

of tape units required = 2(A 1)

number of input volumes: 15

number of areas = 4

number of areas = 32

of tape units required = 3

number of input volumes: 1

number of areas = 3

number of areas = 17

of tape units required = Thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae greater of 4 and A   2

number of input volumes: 15

number of areas = 4

.8 Programmer'sGuide

Maximum number of areas = 17

= Number of input volumes

: These formulas are based on work units 2400 feet long, of the same density as the

volumes, or 3480 tape cartridges used as work units.

Considerations Concerning SyncSort's Disk Space Management on

Data Sets

implements the automatic space management facility by reading the JFCB and

the SPACE parameter to enter a secondary allocation quantity (or accept one

was coded) and the RLSE subparameter. The JFCB is the MVS control block that

the DD statement.

SyncSort options may be implemented which affect the disk space management

the sort. (See the Default Options chapter of the Installhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aation Guide.) Specific functions

these features are as follows.

.The automatic use of secondary allocation and/or release can be selectively sup-

.

amount of secondary space per allocation can be modified.

use of RLSE can be suppressed.

use of space release is suppressed for small sorts, including the in-core sort, in

to minimize system overhead.For non-in-core sorts, if the file size is less than

megabytes, space release is normally suppressed. The 4 megabytes threshold may

altered.

use of space release is normally suppressed for all invoked sorts to prevent SORT

EXCEEDED termination when SyncSort is invoked more than once by

single program. If the first sort involves a modest volume of data, and causes space

to make the work data sets smaller, and the second sort is larger, the secondhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

might not find sufficient work space. Your installation can turn on space release

invoked sorts and thus save disk space. This very rarely causes problems because

(1) few programs invoke the sort more than once and (2) SyncSort's automatic sec-

allocation normally prevents a SORT CAPACITY EXCEEDED termination.

can routinely DYNALLOC data sets for every run.2.3.4.5.6.

factors which may result in suppression of these features include:

.Automatic release is suppressed for permanent data sets unless additional sort work

has been allocated.

12. Performance Considerations12.9

2.Automatic release is normally suppressed by the installation for initiator-dedicated

sets.

uses normal MVS facilities to obtain secondary allocations on work data sets.

, the sort, like any other proghttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aram under MVS, is restricted to sixteen extents

data set. SyncSort, however, will recover from system B37 ABENDS that other pro-

might encounter in attempting secondary allocations. If SyncSort determines that

particular sort work data set cannot sustain a secondary allocation because it already

sixteen extents or because there is not enough space left on the volume, it does not

secondary allocation on that data set. SyncSort further checks all other work data

, and if none of them can sustain a secondary allocation, it must abort with SORT

EXCEEDED.

often avoids the use of one or more work data sets to minimize overall system

, as, for instance, between SORTIN and a work data set. It may obtain secondary

on some data sets while releasing on others.

Coding and Use of Checkpoint-Restart://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar, a hardware failure may prevent the successful completion of a sort or

. Examples include a physically defective output volume or device, or a failure of

operating system for reasons unrelated to the sort.Since sorts tend to consume more

resources than any other type of application, it may be advantageous to be able

resume execution just before the failure occurred rather than restart the job at the

of the failed job step. SyncSort provides this restart capability through its

of the standard OS/MVS Checkpoint-Restart feature.

instruct SyncSort to take checkpoints, code CKPT or CHKPT (either spelling) on the

/MERGE control statement and supply a SORTCKPT DD statement.

a sort, checkpoints are taken at the beginning of Phase 3 before the output data sets

(if any) are opened, and at every end-of-volumehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a of a SORTOUT data set when OUTFIL

not in use.An operator may then restart the sort at Phase 3 or at any end-of-volume

. If necessary, a new output volume or device with identical characteristics to

defective volume or device may be substituted.

a merge or copy, SyncSort takes a checkpoint at every end-of-volume of a SORTOUT

set when OUTFIL is not in use.

cannot be taken within a user exit routine.

DISP Parameter for SORTCKPT, SORTWKnn and SORTOUT Data Sets

coding of the DISP parameter for these data sets depends in part on the

-specified response to an unsuccessful sort. There are four cases:

.10 Programmer'sGuide

NOIOERR and NORC16 (These are the delivered defaults.)IOERR=ABE and RC16=ABEIOERR=ABE and NORC16NOIOERR and RC16=ABE

return code 16 is issued by the unhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asuccessful sort (i.e., when an I/O error occurs and

is set or, for other errors, when NORC16 is set), the second subparameter of

DISP parameter should be specified as KEEP or CATLG. When the unsuccessful sort

a user abend (i.e., when IOERR=ABE for I/O errors, RC16=ABE for other errors),

third subparameter of the DISP parameter should be specified as KEEP or CATLG.

, with NOIOERR and RC16=ABE or with IOERR=ABE and NORC16, both the sec-

and the third DISP subparameter should be specified as KEEP or CATLG. Unless the

parameter is coded in accordance with these two PARM values, restart will be im-

.

is recommended that these data sets be deleted upon successful completion of the sort.

can be done by coding the COND parameter for an IEFBR14 step to follow the sort

in the jobstream.The COND parameter makeshttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the IEFBR14 (data set deletion) ex-

depend upon the successful completion of the previous step (the sort).

SORTCKPT Data Set

a permanent DSN to the SORTCKPT DD statement and specify the UNIT, SPACE

VOL=SER parameters to make the operator's job easier should a deferred restart

necessary.

//SORTCKPT////DDUNIT=3390,DSN=SORT.CKPT,SPACE=(CYL,(1,1)),VOL=SER=WORK01,DISP=(MOD,KEEP,KEEP)

SORTCKPT DD StatementFigure215.

SORTWKnn Data Set(s)

a permanent DSN to every SORTWKnn DD statement and specify the UNIT,

and VOL=SER parameters in case a deferred restart becomes necessary. Avoid

passed data sets, JCL refer-backs, and any other references which would make the

following the restart dependent on the JCL preceding the restart.

that the SORTCKPT data set and the SORTWKnn data http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aset(s) may reside on the

direct access device without loss of efficiency.

12. Performance Considerations12.11

//SORTWK01 ////DD UNIT=3390,DSN=SORT.WK01,SPACE=(CYL,(20,10)),VOL=SER=WORK02,DISP=(,KEEP,KEEP)

SORTCKPT DD StatementFigure216.

Checkpoint-Restart

automatic checkpoint-restart, the operating system will ask the operator whether

unsuccessful/abending step should be restarted. A &quot;yes&quot; reply instructs the system to

the job at the last checkpoint taken. If the operator replies &quot;no&quot;, the job will still

eligible for deferred checkpoint-restart, but its control cards will have to be modified

the job is resubmitted.

requirements for automatic checkpoint-restart are:

The sort step must have a unique name.The JOB statement must specify RD=R andhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a MSGLEVEL=1.All system completion codes with which the sort may abend should be defined at

generation time as being eligible for restart. If the RC16=ABE and/or

=ABE options are in effect, for example, then user abend codes 16 and/or 999

be eligible for restart.

-written exit routines and calling programs may not issue the STIMER macro.

.12 Programmer'sGuide

//AUTOCKPT////XVISORT////SYSOUT //SORTIN //SORTOUT////SORTWK01//////SORTWK02//////SORTCKPT//////SYSINSORT/*JOB(1101,2333),P.ARBEAU,RD=R,MSGLEVEL=(1,1)EXEC PGM=SORT,PARM='RC16=ABE,IOERR=ABE'DDSYSOUT=ADDDSN=XVI.SORTIN,DISP=OLDDDUNIT=TAPE,DISP=(,CATLG,KEEP),DSN=XVI.SORTOUTDDUNIT=3390,DISP=(,DELETE,KEEP),VOL=SER=WORK01,DSN=XVI.SORTWK01,SPACE=(CYL,40)DDUNIT=3390,DISP=(,DELETE,KEEP),VOL=SER=WORK02,DSN=XIV.SORTWK02,SPACE=(CYL,40)DDUNIT=3390,DISP=(,DELETE,KEEP),VOL=SER=WORK02,DSN=XVI.SORTCKPT,SPACE=(CYL,(1,1))http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aDD*FIELDS=(1,10,CH,A),CKPT

.Sample Automatic Checkpoint-Restart JCL Stream

Checkpoint-Restart

automatic checkpoint-restart, deferred checkpoint-restart requires that certain

changes be made before resubmitting the job.

requirements for a deferred restart are:

A SYSCHK DD statement must appear immediately before the first EXEC statement

the job. The SYSCHK DD must use the same DSN name as the SORTCKPT DD

the sort that failed. Specify UNIT, VOL=SER, and DISP=(OLD,KEEP).

RESTART parameter must be specified, and must provide the job stepname and

PROC stepname (if any) associated with the step containing the failed sort, as the

subparameter. (Separate the two stepnames by a period.) The second subpa-

should contain the checkpoint ID of the last checkpoint taken before the sort

. Thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahis can be determined from the console messages given for the job. For JCL

, the ID is usually &quot;Cnnnnnnn,&quot; referring to the sequence number assigned by

operating system.

and SYSIN DD DUMMY statements are permissible if the program is being

at a point where they are no longer needed.

12. Performance Considerations12.13

//DEFCKPT //////SYSCHK //////XVISORT////SYSOUT //SORTIN //SORTOUT////SORTWK01 //////SORTWK02 //////SORTCKPT //////SYSIN

.JOB DD EXEC DD DD DDDDDDDDDD(5433,2333),PAT.TAIG.NANT,RD=R,MSGLEVEL=(1,1),RESTART=(XVISORT,C0000001)UNIT=3390,DISP=(OLD,KEEP),VOL=SER=WORK02,DSN=XVI.SORTCKPTPGM=SORT,PARM='RC16=ABE,IOERR=ABE'SYSOUT=ADUMMYUNIT=TAPE,DISP=(,CATLG,KEEP),DSN=XVI.SORTOUTUNIT=3390,DISP=(OLD,DELETE,KEEP),VOL=SER=WORK01,DSN=XVI.SORTWK01,SPACE=(CYL,40)UNIT=3390,DISP=(OLD,DELETE,KEEP),VOL=SER=WORK02,DSN=SVI.SORTWKhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a02,SPACE=(CYL,40)UNIT=3390,DISP=(MOD,DELETE,KEEP),VOL=SER=WORK02,DSN=XVI.SORTCKPT,SPACE=(CYL,(1,1))DUMMY111111Sample Deferred Checkpoint-Restart JCL Stream

.This JCL differs from automatic checkpoint-restart JCL.

Data Set Placement

Impact of Work Devices on SyncSort

performance of SyncSort is almost totally independent of the number of work data

. The sort's performance may, however, be strongly influenced by the number of de-

to which the work data sets are allocated. Generally, for any sort of significant size,

more work devices, the better the sort can perform. If the sort file size is small, how-

, performance improvements might be outweighed by increased overhead in manag-

the extra data sets.Increasing the number of work devices will:

.

.

.Improve the overlap between CPU and I/O processing.Improve thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe effectiveness of SyncSort's integrated activity monitoring.Reduce the likelihood of SORT CAPACITY EXCEEDED.

.14 Programmer'sGuide

Increasing the number of data sets without increasing the number of devices will only

overhead. It is suggested that, as an initial standard, you implement:

.

.3.4.Four work devices if file size &gt; 100 MB (megabytes).In all cases, allocate one work data set per work device.

Device Separation

easiest way to increase the number of work devices is to increase the number of work

sets. This tends to increase the number of devices to which work data sets allocate,

the relationship between the two may be complex and unpredictable.

to ensure that every sort has at least one work data set on a pack that does not con-

SORTIN or SORTOUT. SyncSort will avoid work data set contention whttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aith SORTIN

SORTOUT if it can.

Separation

to obtain as many paths to the work devices as possible. It is particularly desirable

provide some path to the work data sets that will not be jammed with traffic from

or SORTOUT.

the other hand, SORTIN and SORTOUT may be on the same channel, or even the

device, without any performance loss.

Type Considerations

using a mixture of device types with different track capacities for the work data

, since SyncSort sacrifices some efficiency if this is the case.

you must choose between two different disk device types for the work data sets, use the

; if they are close in speed, use the one with the larger track size.

the use of VIO data sets for work data sets.

you must use tape work data sets, allocate as many as possible.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apter 12. Performance Considerations12.15

12.16 Programmer'sGuide

Chapter 13. The HISTOGRM Utility Program

Is HISTOGRM?

is a separate program which is used to gain information about variable

files.The program scans a variable length file and provides information which can

be used to run more efficient sorts.HISTOGRM can report the:

Block count for minimum and maximum block lengthsRecord count for minimum and maximum record lengthsAverage record lengthTotal number of bytes in the fileTotal number of blocks in the fileL6 value (average work space) for variable length recordsL7 value (segment length) for variable length records

can be used to analyze variable length records in a VSAM entry-sequenced

key-sequenced data set.When HISTOGRM processes a VSAM file only record infor-://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aris gathered; block statistics are not produced.

13. The HISTOGRM Utility Program13.1

Using HISTOGRM to Determine L6 and L7 Values for SyncSort

L6 and L7 values HISTOGRM calculates are passed to SyncSort via the L6, L7

options or the l6, l7 values in the LENGTH parameter of the RECORD control

.(When there is a conflict, the PARM specification takes precedence.)These

are ignored in a merge or copy application.

Parameters for HISTOGRM

control parameters are outlined below; defaults are To specify other

, include a control card in the SYSIN DD portion of the job control stream.Pa-

may appear anywhere through column 71, provided they are separated by

with no intervening blanks.

NRECS=

how many records to scan in the variable length file.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aTH   WIDTH=

the range between minimum and maximum block lengths and the minimum

maximum record lengths in each group of the HISTOGRM output.The number

for the WIDTH value must be a multiple of 4.(4, 8, 12, . . . See examples of block

record HISTOGRMs that follow.)Adjust this range based on the characteristics of

file (the lengths of the shortest and longest record) and the desired length of

.

.2 Programmer'sGuide

DEVWKKEYL

23113330  DEVWK=    33403350      3375 3380  Tells the type of disk device that will be used for intermediate storage when the sort isrun.Specify the device number if HISTOGRM is to calculate L6 and L7. KEYL=        Gives the end location of the last control field in the record.Specify a value for KEYL ifHISTOGRM is to calculate L6 and L7.

=

MAX

thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae maximum number of HIS025I messages that will be issued in a HISTOGRM

.When HISTOGRM processes a large file, this message may be generated as

as once for each record in the file.BIGREC limits the number of HIS025I messages

will be issued in each execution.HISTOGRM processing continues, but no further

are issued once the BIGREC value is reached.

13. The HISTOGRM Utility Program13.3

BLOCK

whether or not to print the graphic portion of the HISTOGRM for block length.

whether or not to print the graphic portion of the HISTOGRM for record length.

BIGSTOP

whether or not to terminate the HISTOGRM run if an RDW value greater than the

LRECL is encountered in the input file.

Control Language

following example shows a sample execution of HISTOGRM.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

.4 Programmer'sGuide

//L6L7//STEP1//STEPLIB //SYSUT1//PGM=HISTOGRMDSN=HISTOGRM,DISP=SHRUNIT=3490,VOL=SER=000001,DSN=VLRECS,LABEL=(1,SL),DISP=OLD//SYSPRINTDDSYSOUT=A//SYSINDD*KEYL=50,DEVWK=3390,NOBLOCK,NOBIGSTP/*JOBEXECDD DD123

.

.Sample JCL/Control Stream for HISTOGRMSYSUT1 is the variable length file to be scanned.Specify the DCB parameter if

is a nonstandard label tape.

is the data set on which printed output will appear.The DCB (not il-

) is:DCB=(LRECL=121,BLKSIZE=121,RECFM=F).

may use DD DUMMY instead of SYSIN DD *.

,DCB=(LRECL=80,RECFM=FB,BLKSIZE=80).Specify //SYSIN DD2.3.

HISTOGRM through an E15 Exit

is possible to execute HISTOGRM during a sort by specifying an E15 exit in the MODS

statement and coding HISTE15 as the r value.This produces a printout of the

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aISTOGRM for Records at the conclusion of the job.(It is, however, not possible to get

printout of the HISTOGRM for Blocks when initiating HISTOGRM in this way.)

following example shows a sample execution of HISTOGRM by an E15 exit during

sort.

13. The HISTOGRM Utility Program13.5

//HISTSORT//STEP2//SORTIN//////SORTOUT//////SORTWK01//SORTWK02//SORTWK03//SYSOUT//MODLIB//SYSINSORTMODS//SYSPRINT//HISTINWIDTH=40/*PGM=SYNCSORTUNIT=3490,VOL=SER=000001,DSN=VARDATA,LABEL=(1,SL),DISP=OLDDDUNIT=3490,VOL=SER=000002,DSN=SORTED.DATA,LABEL=(1,SL),DISP=(,KEEP)DDUNIT=SYSDA,SPACE=(CYL,(20,10))DDUNIT=SYSDA,SPACE=(CYL,(20,10))DDUNIT=SYSDA,SPACE=(CYL,(20,10))DDSYSOUT=ADDDSN=SYS1.SYNCLIB,DISP=SHRDD*FIELDS=(4,10,CH,A)E15=(HISTE15,7400,MODLIB,N)DDSYSOUT=ADD*JOBEXECDD123456789

.Sample JCL/Control Stream for HISTOGRM Initiated by an E15 Exit

.SORTIN is a DD card for SyncSohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1art.It contains the data set that will be analyzed

then sorted.The data set name is VARDATA, and it is found on the standard

tape with the volume serial number 000001.The data set is already in ex-

.If SORTIN is not a standard label tape, DCB parameters must be specified.

that RECFM must be either V, VB, or VBS.

is a DD card for SyncSort.It assigns the data set name SORTED.DATA

the output file, and specifies a 3490 tape unit with the volume serial number

.It is not yet in existence.The DCB parameters default to those of SORTIN.

, SORTWK02, and SORTWK03 are DD cards for SyncSort.They reserve

cylinders of primary space, 10 cylinders of secondary space on direct access devices

intermediate storage.

is a DD card for SyncSort.It assigns the SyncSort messages to the output

associated withttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ah class A.

MODLIB DD statement is used to define the partitioned data set in which the

program resides; MODLIB is referenced in the MODS control statement.

data set name is SYS1.SYNCLIB, and the DISP shows the library may be

.2.3.4.5.

.6 Programmer'sGuide

6.The SYSIN DD * statement marks the beginning of the input stream that includes

sort control statements.The SORT Control Statement shows that one control

will be sorted on.It consists of bytes 4-13 of the record, contains character data,

is to be sorted in ascending order.

MODS control statement must specify an E15 exit as an exit-type parameter and

HISTE15 as the exit routine name.HISTE15 takes 5000 bytes of core storage

resides in the main SyncSort library referenced here by a DD statement named

.The routine does not require link-http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aediting during sort execution.

is the data set on which the printout from HISTE15 appears.Its DCB

: DCB=(LRECL=121,BLKSIZE=121,RECFM=F).

HISTIN DD statement is optional.It is used to override any default values.The

DCB parameter must be specified:DCB=(LRECL=80,RECFM=

,BLKSIZE=80).(With HISTIN DD *, the DCB is not necessary.)7.8.9.

for HISTE15

=

=

=

=ALL20The same SORTWK devices used in executing this sort.End of key field furthest into record for this sort.

=0 (This cannot be overridden.)

(This cannot be overridden.)

(This cannot be overridden.)

13. The HISTOGRM Utility Program13.7

13.81 HIS007I HIS008I HIS009I BLOCK COUNT 3 18 80 145 205 253 197 .....................................................................................http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a..... .****** . .************************** . .************************************************ . .******************************************************************** . .************************************************************************************ . .***************************************************************** . .......................................................................................... NUMBER OF BLOCKS................. TOTAL LENGTH OF ALL BLOCKS....... AVERAGE BLOCK LENGTH............. 898 104119 116 BLOCK LENGTH MIN MAX 40 60 80 100 120 140 59 79 99 119 139 159

's Guide 1. 2. 3.

Contents of HISTOGRM Output

informational messages for blocks are printed at the top of the report. For explanations, see individual messages in the message section which follows these examples. BLOCK COUNT gives the number of blocks falling within the minimum and maximum http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anumbers shown as BLOCK LENGTH. The range is the WIDTH value that has been specified. The asterisks are the graphic representation of the number of blocks within the range of block lengths.

[此处图片未下载成功]

1

I HISO11I HIS012I HIS016I HIS015I HIS014I HIS017I HIS018I HISO19I HIS005I HIS023I HIS020I

OF RECORDS.............. TOTAL LENGTH OF ALL RECORDS.... AVERAGE RECORD LENGTH.......... KEY LENGTH..................... AVERAGE SPACE PER RECORD - L6.. RECOMMENDED SEG. SIZE - L7..... LINE WIDTH..................... LONGEST RECORD................. SHORTEST RECORD................ RECORDS TOO LONG............... RECORDS TOO SHORT.............. DEVICE TYPE....................

93412 98 50 129 72 20 155 40 48 41 3390 RECORD LENGTH MIN MAX 40 60 80 100 120 140 59 79 99 119 139 159

RECORD COUNT ......................................................................................... 104http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a .********************************** . 181 .*

*********************************************************** . 199 .***************************************************************** . 196 .**************************************************************** . 211 .********************************************************************* . 61 .******************** . .........................................................................................

13. The HISTOGRM Utility Program 13.9

Contents of HISTOGRM Output

.

informational messages for records are printed at the top of the report. For explanations, see individual messages in the message section which follows these examples. RECORD COUNT gives the number of records falling within the minimum and maximum numbers shown as RECORD LENGTH. The range is the WIDTH value that has been specified. The asterisks are the graphhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aic representation of the number of records within this range of record lengths.

.

.

[此处图片未下载成功]

HISTOGRM Messages

indicate a critical error condition.HISTOGRM terminates to

you to correct the error(s) so that a successful program may be run.

are informational or indicate a non-critical error.They are

on the HISTOGRM output for blocks and records and contain

information inserted by HISTOGRM.

CONTROL CARD

:A blank control card or an incomplete control parame-

was found.

DATA ON CONTROL CARD

:An invalid control parameter was found.

CONTIN NOT FOUND

:Control card continuation was indicated either by a

-blank character in column 72 or by a comma immediately after the

control field, but nohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a continuation card was found.

DCB OR ACB DATA

:The SYSUT1 data set was opened and one of three er-

was detected:(1) LRECL was not specified, (2) BLKSIZE was not

, (3) RECFM was not V, VB, or VBS, or (4) the data set is a

RRDS.

:Check for a missing DCB parameter if SYSUT1 is a non-

label tape.If the file is a standard label tape or a disk file, one

the DCB subparameters may be missing, or the file is not a variable

file.

TOO LONG nnnn

:Records with lengths exceeding the length specified in

DCB were found.The nnnn represents the number of long records

.Long records have no effect on other HISTOGRM statistics.

SPAN CONTROL FIELD BLOCK nnnn LOGICAL RE-

nnnn DATA SET # nnnn

:The third byte of the four byte recorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad descriptor word

a variable length record does not contain a valid code X'00',

'01', X'10', X'11', or the code is inconsistent with the code of the previous

.The block and record number being processed are included in

message text.The first 100 bytes of both current and previous seg-

along with their RDWs, follows this message.DATA SET # will be

concatenation number within SYSUT1 if the input data set is con-

.HISnnnIHIS001AHIS002AHIS003AHIS004AHIS005IHIS006A

.10 Programmer'sGuide

HIS007I

I

I

I

I

I

I

I

INUMBER OF BLOCKS nnnnEXPLANATION:The total number of blocks read from the SYSUT1 dataset is given on the HISTOGRM for blocks.TOTAL LENGTH OF ALL BLOCKS nnnnEXPLANATION:The total length in bytes of all blocks read is given onhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe HISTOGRM for blocks.AVERAGE BLOCK LENGTH nnnnEXPLANATION:The average block length of all blocks read is given onthe HISTOGRM for blocks.NUMBER OF RECORDS nnnnEXPLANATION:The total number of records read from the SYSUT1data set is given on the HISTOGRM for records.The total will excludeany records with lengths greater than the length specified in the DCB.TOTAL LENGTH OF ALL RECORDS nnnnEXPLANATION:The total length in bytes of all records read is given onthe HISTOGRM for records.AVERAGE RECORD LENGTH nnnnEXPLANATION:The total length of all records is divided by the numberof records and the quotient is given on the HISTOGRM for records.NUMBER OF SPANNED RECORDSEXPLANATION:The number of records contained within two or moreblocks is given on the HISTOGRM for records.RECOMMENDED SEG. SIZE - L7EXPLANATION:The recommended segment size is given on theHISTOGRM for records.Supply SyncSort with this value either throughL7 in the PARM fieldhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a of the EXEC statement or through l7 in theLENGTH parameter of the RECORD control statement.Note:If the recommended number is 0, the range of record lengths in thefile was too wide to compute an optimal value.In this case, do not supplyan L7.AVERAGE SPACE PER RECORD - L6

:The average work space necessary for each record is

on the HISTOGRM for records.Supply SyncSort with this value

through L6 in the PARM field of the EXEC statement or through

in the LENGTH parameter of the RECORD control statement.

:If the recommended number is 0, the range of record lengths in the

was too wide to compute an optimal value.In this case, do not supply

L6.

13. The HISTOGRM Utility Program13.11

HIS016IKEY LENGTH nnnn

:The end location of the last control field in the record

given on the HISTOGRM for records.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arLINE WIDTH nnnn

:The numeric interval between the minimum and max-

block/record length is given on the HISTOGRM for records.

RECORD nnnn

:The length of the longest record read; that is the record

the largest value in the record descriptor word.

DEVICE TYPE

:An invalid device type was specified on the control card

the SYSIN data set.

RECORD nnnn

:The length of the shortest record read is given on the

for records.

TYPE nnnnnn

:The type of intermediate storage device to be used for

sort is given on the HISTOGRM for records.

PARAMETER IGNORED

:Information about blocks cannot be collected when

HISTE15 during a sort.

FILE IS EMPTY

:There are no rechttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aords in the input file which are not

than the data set's LRECL.

TOO SHORT nnnn

:Records with lengths less than the KEYL value speci-

for the HISTOGRM execution were found.The nnnn is the number

short variable length records in the file.

nnnnn,BLKSIZE nnnnn,RECFM xxx

:The logical record length, block size, and record format

the input data set obtained from the SYSUT1 DCB after OPEN.

RDW/RECORD LENGTH BLOCK nnnn LOGICAL RE-

nnnn DATA SET # nnnn

:The RDW value of the current record is greater than

DCB LRECL and HISTOGRM has been requested to terminate (thru

BIGSTOP parameter).The block and record number are supplied in

message and the first 100 bytes of the record and the RDW follow the

.DATA SET # will be the concatenation number withttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahin

, if the input data set is concatenated.HIS017IHIS018IHIS019AHIS019IHIS020IHIS021IHIS022AHIS023IHIS024IHIS025A

.12 Programmer'sGuide

HIS025I

I

A

A

A

A

AINVALID RDW/RECORD LENGTH BLOCK nnnn LOGICAL RE-CORD nnnn DATA SET # nnnnEXPLANATION:The RDW value of a record is greater than the DCBLRECL.Block number and record number are supplied in the messagetext, along with the concatenation number if SYSUT1 is concatenated.INPUT DATA SET IS VSAM ... NO BLOCK STATISTICS GATH-EREDEXPLANATION:The input to HISTOGRM is a VSAM data set; thereforeblock statistics are not produced for this HISTOGRM execution.SYSUT1 DD STATEMENT MISSINGEXPLANATION:The input data set is absent; the HISTOGRM run hasterminated.VSAM LOGICAL ERROR nnEXPLANATION:An error occurred while reading a VSAM data set.Forthe definition of the error number, nn, consulthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a one of the following IBMpublications: MVS/XA VSAM Administration: Macro Instruction Reference,CG26-4016 MVS/DFP Macro Instructions for Data Sets, SC26-4747 DFSMS/MVS Macro Instructions for Data Sets, SC26-4913VSAM OPEN ERROR nnEXPLANATION:An error occurred during an attempt to OPEN a VSAMfile.For the definition of the error number, nn, consult one of the fol-lowing IBM publications: MVS/XA VSAM Administration: Macro Instruction Reference,CG26-4016 MVS/DFP Macro Instructions for Data Sets, SC26-4747 DFSMS/MVS Macro Instructions for Data Sets, SC26-4913messagetextEXPLANATION:An I/O error has occurred. The message text gives adetailed description of the error.INVALID BDW ENCOUNTERED BLOCK nnnn

:The block descriptor word for block number nnnn, was

zero or greater than the DCB blocksize.

13. The HISTOGRM Utility Program13.13

13.14 Programmer'sGuide

Chapter 14. Value-Addedhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Products

chapter describes SyncSort's three value-added products:

SyncSort/COBOLAdvantagePROC SYNCSORT - An Accelerator for SAS&#174; SortingPipeSort

products significantly improve sorting efficiency and enhance programmer pro-ductivity.

/COBOL Advantage

SyncSort/COBOL Advantage is a fully automatic facility for improving the perform-ance of all COBOL programs that invoke SyncSort MVS. By enhancing and replacingCOBOL sort interfaces, it will improve elapsed time by 25 to 40%.It will significantlyreduce CPU time and EXCPs in addition to elapsed time in COBOL sorts with USINGand/or GIVING clauses.

SyncSort/COBOL Advantage is transparent to the user. It is invoked dynamicallywhenever SyncSort is invoked, and it automatically decides how to accelerate COBOLprocessing.

SyncSort/COBOL Advantage is easy to install and requires no changes thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ao existingprograms or procedures. Programs do not have to be recompiled to benefit from theSyncSort/COBOL Advantage.

more information regarding the benefits and installation of this product, refer to theSyncSort/COBOL Advantage Installation and Use Guide.

14. Value-Added Products14.1

PROC SYNCSORT - An Accelerator for SAS&#174; Sorting

SYNCSORT - An Accelerator for SAS&#174; Sorting is a high performance replacementfor the SAS-provided procedure PROC SORT. Compared to PROC SORT, PROCSYNCSORT reduces the resources required for sorting within SAS applications and sig-nificantly cuts sort elapsed time.

processing within SAS often consumes as much as 30 percent of CPU time andEXCPs. Because sorting is such a large part of system activity, PROC SYNCSORT's effi-ciency results in noticeable improvements in overall system throughput. This reducedelapsed time from PROC SYNCSORT makehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as it possible for SAS applications to completemuch faster.

SYNCSORT improves performance by providing a direct interface betweenSyncSort and SAS.This frees SyncSort to use its high performance techniques - sophis-ticated access methods, path length minimization algorithms and I/O optimization.No modifications to SyncSort are required to install and use PROC SYNCSORT.

more detailed information regarding the use and installation of PROC SYNCSORT,refer to the booklet titled PROC SYNCSORT - An Accelerator for SAS&#174; Sorting: Instal-lation and Use Guide.

works with SyncSort to run multiple sorts simultaneously on the same inputdata.For large input files, PipeSort significantly reduces total elapsed time compared torunning separate sort jobs.

reads SORTIN once and distributes the input records to up to eight simultane-ous SyncSort executions.The complete range of Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ayncSort control statements and PARMsis available for the individual sort operations.

output files are differently sequenced according to user-specified sort keys and arewritten to different SRTnOUT DD data sets.

, you can use an inline E15 exit, with or without one or more E35 exits.Aninline E15 input exit can supply the input data to PipeSort, and E35 output exits canaccept the different output record sets.

detailed information regarding installation and implementation through MVS JCL,refer to the PipeSort User's Guide.

.2 Programmer'sGuide

Chapter 15. Messages

messages issued by SyncSort have the form:

Message text

nnn is the message number and x may be any of the letters A through I. The in-terpretation of the suffix letter x is given below.

(action) message indicates a critical error condition:SyncSort terminates in order tohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aallow the user to correct the error(s) so that a successful sort/merge may be run. ExampleWER002AEXCESSCARDS

(tuning) messages provide information that may be useful in adjusting the job/controlstream to the actual demands of the job. These messages only print if a critical errorforces sort termination or if B messages were requested at execution or installation time.Example WER151BSECONDARY EXTENTS OBTAINED xxx

-I (informational) messages document decisions internal to the sort as well asSyncSort's response to error conditions which are not severe enough to warrantsort/merge termination.

WER177I

ITURNAROUND SORT PERFORMEDSORTIN DCBBLK GT ACTUAL, I/O INEFF

MVS provides an interactive message explanation facility, SS37MSG, that givesonline access to all SyncSort message texts and their explanations by message number.If SS37MSG is included as an option in a PDF menu, you http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amay invoke from that menu.

15. Messages15.1

Otherwise, you may invoke SS37MSG from the command line of any ISPF panel by en-tering the following command:TSO %SS37MSG

installation of the SS37MSG facility is optional. Therefore, if you are unable to invokethe facility as described, you should contact your system administrator for more infor-mation.

:All messages that refer to SORTIN, SORTWK, SORTOF and SORTOUT providethe actual DD name, which reflects any changes made via a prefix override.

ACOL 1 OR 1-15 NOT BLANK

: This message is triggered by a character in column 1 of the

control statement or in columns 1-15 of a continuation statement fol-

a statement with a character in column 72, or by a non-blank char-

in columns 1-15 of a sort control statement in the $ORTPARM data set.

columns must be left blank.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aarA EXCESSCARDS

: The static internal storage area is inadequate for the

and/or complexity of the control statements in this application. Ei-

the minimum storage value set at installation time is too low, or insuf-

storage is available in your region.

: Ask the systems programmer in charge of SyncSort installation to

the minimum storage (MINCORE) value unless the storage avail-

in the region is less than the minimum storage value. In that case, in-

the storage available in the region or partition so that it at least

the minimum storage value.

ANO CONTIN CARD

: A continuation statement was indicated by a non-blank

in column 72 of a control statement or by a control statement

in an operand-comma combination; no continuation statement fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aol-

.

AINVALID OP DELIMITER

: A control statement ends with an incorrect delimiter, such

a comma.

ASTMT DEFINER ERR

: A control statement contains an invalid operation name.

(Tape Sort accepts fewer operation names than Disk Sort, MAXSORT and

.)

.2 Programmer'sGuide

WER006AOP DEFINER ERR

: An operation name must be followed by an operand on thesame control statement.

ASYNTAX ERROR - S/M,REC,MOD

: The control statement shown in the message contains asyntax error.

AFLD OR VALUE GT 8 CHAR - S/M,REC,MOD

I

A

A

A

A

A

A

AEXPLANATION: A parameter exceeds eight characters on the statementshown in the message.EXCESS INFO ON CARD - S/M, REC,MODEXPLANAThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aION: The control statement shown in the message contains moreinformation than necessary.This excess information will be treated as acomment.NO S/M CARDEXPLANATION: The SORT/MERGE control statement is required for allSyncSort applications including a straight copy (coded SORT FIELDS=COPYor MERGE FIELDS=COPY).TOO MANY S/M KEYWORDSEXPLANATION: The maximum of eight keyword operands for tape sort wasexceeded on a control statement.NO FLD DEFINEREXPLANATION: The FIELDS operand was not specified on theSORT/MERGE control statement.INVALID S/M KEYWORDEXPLANATION: An invalid keyword operand was found on theSORT/MERGE control statement.DUPLICATE S/M KEYWORDEXPLANATION: A keyword operand was defined more than once on theSORT/MERGE control statement.TOO MANY PARAMETERSEXPLANATION: A keyword operand on the SORT/MERGE control state-ment contains too many parameters.INVALID VALUES IN FLD

: An invalid value was specified in the FIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aELDS operand onthe SORT/MERGE control statement.

15. Messages15.3

WER017AERR IN DISP LENGTH VALUE

: The length and displacement value of a control field isgreater than 4092 (4084 for variable-length records), or less than one, or thesum of the lengths of all control fields exceeds 4092 (4084 for variable-lengthrecords).

ACTL FLD ERR

: An error was detected in the SORT/MERGE control state-ment for the data format of a control field.The format was specified for onefield but not for another, or bit comparisons were specified and FORMAT=BIwas not specified.

A SIZE/SKIPRECERR

: The SIZE or SKIPREC parameter was incorrectly speci-fied.

AINVALID REC KEYWORD

: An invalid keyword was detected in a RECORD controlstatement.

ANO TYPE DEFINER

: The TYPE operand must be specified inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a the RECORDcontrol statement.

ARCD FORMAT NOT F/V

: An invalid RECFM was detected for SORTIN orSORTOUT.

ANO LENGTH DEFINER

: The LENGTH operand must be specified on the RECORDcontrol statement.

AERR IN LENGTH VALUE

: An invalid LENGTH subparameter was found in a RE-CORD control statement. For example, l5 was greater than l1 or l4 wasgreater than l2.

ARCD SIZE GT MAX

: The LENGTH operand in a RECORD control statementspecified a value which is greater than the maximum value allowed (32,767).

AL1 NOT GIVEN

: The LENGTH operand on a RECORD control statementdoes not contain an l1 value.

ACONTROL FIELD BEYOND RECORD

: The last byte of a SORT/MERGE control field is locatedbeyond the maximum record length specified, or a variable length record isshorter thahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an the ending location of a specified control field in an executionfor which this is defined as cause for SyncSort termination (see VLTEST).

.4 Programmer'sGuide

Program HISTOGRM may be used to determine the length of the shortestrecord in the input file.

ATOO MANY EXITS

: More than the maximum number of exits allowed (16) werespecified.

A IMPROPEREXIT

A

A

A

A

A

A

BEXPLANATION: The set of legal exits depends on the sorting techniquechosen.Tape Sort does not support E14 or E32; a merge or copy may notspecify any Phase 1 or Phase 2 exits; a copy may not specify exit E32 or E61;and a sort or merge with data fields of Y2x or PD0 formats may not specifyexit E61.MULTIPLY DEFINED EXITEXPLANATION: The same program exit was specified twice on a MODScontrol statement.INVALID MODS OP CHAREXPLAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aNATION: An invalid character was detected in a parameter on aMODS control statement.EXIT E61 REQUIREDEXPLANATION: A SORT control statement specified &quot;E&quot; in the FIELDSparameter but program exit E61 was not specified on a MODS controlstatement.CONTROL FIELD COLLATING ORDER E REQUIREDEXPLANATION: Program exit E61 was specified on the MODS controlstatement but &quot;E&quot; was not specified in the FIELDS parameter of the SORTcontrol statement.PARAM ERR FOR MODSEXPLANATION: An incorrect number of parameters was given for an oper-and on a MODS control statement, or SYSIN was specified on a MODScontrol statement as the source for user exit routines but a //SORTMODSor //SYSIN statement is missing or dummy.DUPLICATE MOD RTN IN PHASEEXPLANATION: The same exit routine was used for more than one programexit in the same phase of a tape sort, or two or more exit routines in a tapesort have the same name.G=ggg, B=bbb, SEGLEN=sss, BIAS=http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1azz

: The tuning information displayed is as follows:

=gggggg is the number of records that can be contained in

's working virtual storage area. For variable length

, this number is the number of segments.

15. Messages15.5

B=bbbbbb indicates the physical blocking used for intermediate

.For fixed length records, this number represents

factor.For variable length records, it repres-

the blocksize. The B value will not appear in the mes-

for incore or turnaround sorts.

value appears in the message for variable length re-

, when the execution is not an incore or turnaround

. It reflects the segment length used in SyncSort's

storage during Phase 1.

reflects the degree of prior sequencing in the input data.

number displayed ranges from http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a00 to 99 indicating ran-

to highly sequenced input. The BIAS value is not in-

in the message for an incore or turnaround sort,

it is 100 by definition.SEGLEN=sssBIAS=zz

AREXX ENVIRONMENT UNAVAILABLE

: One or more REXX exits were specified in a MODS controlstatement, but the required operating system and/or TSO environment is notavailable.

AINSUFFICIENT VIRTUAL STORAGE

: The amount of virtual storage available to SyncSort is notlarge enough to permit execution. Refer to the &quot;Setting CORE&quot; section of thePerformance Considerations chapter for further information.

: Verify that virtual storage is specified properly.Check that theregion size is sufficient for execution.

AINSUFFICIENT WORK UNITS

: Tape Sort requires at least three work devices, numberedin order.

AN GT MAX://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aar: The number of records specified in the SIZE parameter ona SORT control statement is greater than the NMAX value calculated bySyncSort.

: Check SIZE parameter for error. If there is no error, increaseintermediate storage.

AUNITS ASSGN ERROR

: The device type of a SORTWK data set is not valid.

ADATA SET ATTRIBUTES NOT SPECIFIED

: The DCB parameter was not specified for a SORTIN orSORTOUT data set.

: Specify the DCB parameters. When including an E18 exit routine,this is necessary even when SORTIN is a standard labeled tape.

.6 Programmer'sGuide

WER044AEXIT Exx INVALID OPTION

: The exit routine shown in the message specified an invalidoption for the modification of a DCB parameter of a sort/merge data set.

CEND SORT PH

:SyncSort has completed its sort phase.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arWER046ASORT CAPACITY EXCEEDED

A

I

I

IEXPLANATION: All available intermediate storage is exhausted, includingany secondary allocation allowed in this job set.Sort processing cannotcontinue.ACTION: Supply more intermediate storage (see the SORTWK calculationformula) or use the MAXSORT technique.RCD CNT OFF, IN x, OUT yEXPLANATION:The actual number of records specified in the SIZE pa-rameter on the SORT control statement (the IN value) was not equal to thenumber of records read from the SORTIN data set (the OUT value). (Thiscomparison is made only when the SIZE parameter specifies an actualnumber of records.)For Disk Sort, MAXSORT and PARASORT:the actual number of records(the IN value) for FILSZ=n specified either on the SORT control statementor as a PARM option was not equal to the total number of records (the OUTvalue) from the SORTIN data set after any changes due to theINCLUDE/Ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aMIT control statement, and an E14 or E15 exit routine, andSKIPREC and/or STOPAFT processing.For Tape Sort only: there is a discrepancy between the number of recordsentering and leaving a phase which is not accounted for by user exits (thisis usually caused by an I/O error - try running the sort again).E16 EXIT CALLEDEXPLANATION: Program exit E16 was entered after all availableSORTWORK space was exhausted.SUM FIELD OVERFLOWEXPLANATION: Summarization of two equally keyed records could not bedone due to a numeric overflow in a defined SUM field.As a result, bothrecords were written to the output data set.ACTION: If complete summarization is desired, use the INREC controlstatement to pad the fields with leading zeros of the proper numeric format.Adjust the SUM field and other control statement fields accordingly.SUM CONTROL STATEMENT IGNORED

: A SUM control statement was specified in a SORTFIELDS=COPY application. Sinhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ace a COPY operation does not useSORT/MERGE key fields, the specification of SUM, which operates onequally keyed records, is illogical.

15. Messages15.7

ACTION: The SUM statement will be ignored, but the application should bechecked for correct specification of control statements.

A UNENDINGMERGE

:The intermediate storage provided is insufficient to com-plete the intermediate merge phase.

: Assign more tape work units to the sort.

IEND SYNCSORT - jobname, stepname, procstepname,

=hhhh,hhhh,...

: SyncSort has successfully completed execution. Thehexadecimal information following the DIAG keyword is likely to changefrom execution to execution. It is internal diagnostic information intendedfor use by SyncSort personnel in Product Support.

AOUT OF SEQ

: The current record leaving the final merge phhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aase is not incollating sequence with the last record blocked for output.

IRCD IN x, OUT y

: The x represents the number of records read from the inputdata set(s).If OUTFIL statements are not present, the y represents thenumber of records in the output file. If OUTFIL statements are present, they represents the number of records available for OUTFIL processing.INSERT x, DELETE y

: The x represents the number of records inserted by userexit routines. The y represents the number of records deleted by user exitroutines, SUM, and INCLUDE/OMIT control statements. NOTE: ForMAXSORT, these counts are cumulative for the entire MAXSORT applica-tion.WER055I

ASORTIN/SORTOUT NOT DEFINED

: A required SORTIN or SORTOUT DD statement could notbe found.

ASORTIN NOT SORTWK01

: A tape work data set other than SORTWK01 is assignedto the same tahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ape unit assigned to SORTIN.

ASORTOUT A WORK UNIT

: A tape work data set is assigned to the same tape unitassigned to SORTOUT.

ARCD LNG INVALID FOR DEVICE

: The logical record length specified for a fixed length inputdata set plus overhead, if any, is too large to fit on one disk track of theintermediate storage device, or (Tape Sort only) it is less than 18 bytes long.

.8 Programmer'sGuide

WER060ADSCB NOT DEFINED

:There are no DD names in the TIOT for any of the sort

data sets.

AI/O ERR jobname, stepname, unit address, device type, DDname,WER062A

A

A

A

A

Ioperation attempted, error description, last seek address or blockcount, access method.EXPLANATION: An I/O error has occurred on the device whose address isgiven. I/O errors are often transient -http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a resubmitting the job may result in asuccessful run. However, if the I/Oerror is on SORTIN, the following shouldbe checked first:1.When SORTIN consists of concatenated data sets, check that the dataset with the largest blocksize is specified first.2.If the data set is on disk and has just been created by another program,check that this program opened the data set even if no data was writtento the file. The data set must be opened in order for an end-of-file markto be written. (In the absence of an end-of-file mark, SyncSort will tendto read whatever was on the disk as part of SORTIN, causing an I/Oerror.)L E ERREXPLANATION: The linkage editor detects an error so serious that exe-cution cannot continue.xxxxxx OPEN ERREXPLANATION: The data set shown cannot be successfully opened.ACTION: Check for missing DD statements.DELETEERREXPLANATION: A SyncSort program module is unable to delete itself or auser exit routine.DECK STRUCTURE ERRORhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aEXPLANATION: The end of the SYSIN data set was reached before all userexit routines were read or an object deck was missing its first statement.APPROX RCD CNT xEXPLANATION: Sort capacity was exceeded, so the sort terminated. Theapproximate number of records processed by SyncSort up to this point isgiven.INVALID EXEC OR ATTACH PARAMETER

: An invalid parameter was detected in the PARM field of

EXEC statement or in the parameter list if SyncSort was initiated

ATTACH, LINK, or XCTL. Invalid parameters are ignored. (If a

is entered more than once, the last entry, if valid, is used.)

15. Messages15.9

WER068AOUT OF SEQ SORTINxx[, BLOCK y]

: A record in the SORTIN data set indicated by xx is out of

according to the FIELDS specification on the MERGE statement.

number y of the block containing the out-of-sequence http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arecord is given if

E32 exit was not used.

A E39/OUTFILINCOMPATIBLE

: The E39 exit facility may not be utilized in sorts/merges

also specify OUTFIL control statements.

Addname TOTAL,SUBTOTAL,AVG,SUBAVG FIELD OVERFLOW

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.An overflow

was generated during the TOTAL, SUBTOTAL, AVG or SUBAVG

function for the specified output file.All fields are totaled inter-

as 8-byte PD values, allowing for 15 decimal digits.

: This error is usually due to invalid data in the specified fields.

the fields specified in the indicated parameter and check the actual

in those fields to ensure that no total will exceed 15 decimal digits.In

cases, within TRAILER2 or TRAILER3, you http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acould change SUBTOTAL

TOTAL or SUBAVG to AVG to reduce the possibility of overflow.

AMAXIMUM NUMBER OF RECORDS EXCEEDED

:SyncSort's default internal limit on the maximum number

records that can be sorted has been exceeded.By default, the internal

on the number of records that can be processed for variable length data

for a sort application that uses the EQUALS option is 4,294,967,295 re-

.Specify the EXTCOUNT PARM to increase the internal limit to

,737,488,355,327 records. Fixed length sorts without EQUALS have au-

support for the maximum number of records allowed by the

PARM.For additional information, see the EXTCOUNT option

the &quot;PARM Options&quot; chapter.

ADUPLICATE RECORD KEYWORD

: A keyword operand was defined twice on a RECORD con-

statement.://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aparDINVALID TAPE TYPE IN PARM FIELD

: An invalid tape type was specified for DEVIN/DEVOUT in

PARM field of the EXEC statement. SyncSort ignored the invalid pa-

.

ACOBEXIT=COB2 AND COBOL E15 AND E35 EXITS FOUND IN COPY

:A COBOL E15 and COBOL E35 may not both be specified

a copy application if COBEXIT=COB2 is in effect. Only one of the exits is

.

.10 Programmer'sGuide

WER103DINVALID MESSAGE TYPE IN PARM FIELD

: An invalid message code was specified in the PARM field

the EXEC statement or in the invoking program parameter list. SyncSort

the invalid parameter.

AREXX E15 AND REXX E35 EXITS FOUND IN A COPY APPLICATION

:A REXX E15 and a REXX E35 may not both be specified

a copy application.Only one of the exits http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ais permitted.

AINCOMPATIBLE LEVELS BETWEEN THE STATIC AND DYNAMICWER106A

A

I

I

ILIBRARIES OF A COBOL OR C EXITEXPLANATION:When using either a C or COBOL exit, insure that therun-time dynamic Language Environment libraries are at the same or higherlevel than the libraries used for the compile or link-edit of the exit.ddname INVALID DEVICE TYPEEXPLANATION:The ddname is either SORTIN, SORTINnn, SORTOUT,SORTOFxx, SORTOFx or the ddname provided by an OUTFIL FNAMESparameter.This file resides on an invalid device type. Valid device typesinclude the IBM 2305, 2314, 3330, 3330-11, 3340, 3344, 3350, 3375, 3380,3390, and 9345 direct access devices and 3850 mass storage systems, andtheir equivalent as well as the IBM 2400, 3400, 3480, 3490 and 3590 seriestape devices and their equivalents.ddname RECFM INCOMPATIBLE WITH REPORT WRITINGEXPLANATION:The ddname will be SORTOUT, SORTOFxhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ax, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.The RECFMspecified for the file did not include the 'A' (ASA control character) specifi-cation that is required when report writing is requested.SORTIN: RECFM=;LRECL=;BLKSIZE=,CISIZE= [;CINV ACCESS]EXPLANATION:This informational message lists the DCB characteristicsused by SyncSort to process the SORTIN file. For a non-VSAM data set thatis concatenated, the DCB characteristics are for the first of the concatenateddata sets, except for BLKSIZE, which is the largest of all data sets in theconcatenation examined at sort initialization time. For a VSAM data set, theCISIZE is provided; if control interval access was used, the CINV ACCESSportion of the message will be displayed.MERGE INPUT: TYPE=F,V;LRECL=EXPLANATION: This informational message lists the DCB characteristicsused by SyncSort to process the input files for a merge.ddname RECFM= ;LRECL= ;BLKSIZE=,CISIZE= [;http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aCINV ACCESS]

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.This infor-

message lists the DCB characteristics used by SyncSort to process

indicated output file.This message will be provided for each output file

15. Messages15.11

specified.For a VSAM data set, the CISIZE is provided; if control interval

was used, the CINV ACCESS portion of the message will be displayed.

A [ddname]INREC,OUTREC,TOTAL/SUBTOTAL,MIN/SUBMIN,

/SUBMAX,AVG/SUBAVG INVALID DATA CONVERSION

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.Data conver-

has been requested for INREC, OUTREC, OUTFIL OUTREC,

/SUBTOTAL, etc., as indicated, and one of the following error condi-

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as has occurred:

.

.The length of the field to be converted is too large.Data conversion has been requested for a field that is not specified as

, CSF/FS, FI, PD, Y2ID, Y2IP or ZD.

or conflicting EDIT/SIGNS parameters were specified.3.

AINVALID VALUES IN FIELD PARAMETER

: An invalid value was specified in the FIELDS operand of

SORT/MERGE control statement.

ATOO MANY SORT FIELDS

: The number of sort control fields specified exceeds the

limits of the product. The absolute upper limit on the number of sort

fields is 128; however, depending on the complexity of an application,

limit may be reduced.When locale processing is used, the number of

CH control fields is also limited by the length of those fields.

AILLEGAL MOD NAME

: An invalid http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aname for a program exit was entered on a

control statement.

ATHE FOLLOWING H/T IS GT LRECL:

:This message flags any HEADERs or TRAILERs that ex-

the LRECL specification. The HEADER or TRAILER in error will be

on the next line.

AINVALID ANSI CONTROL CHARACTER FOUND

: An invalid ANSI control character appears in a HEADER

TRAILER. The ANSI Control Character Table lists the valid characters

by SyncSort.

IINVALID ANSI CONTROL CHARACTER FOUND

:An invalid ANSI control character appears in an output

record. The sort will process the record as if a blank control character

been found. This message will be issued only once regardless of how

data records have invalid ANSI characters. The ANSI Control Char-

Table lists the valid characters achttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acepted by SyncSort.

.12 Programmer'sGuide

WER118Addname ILLEGAL OVERLAPPING FIELDS

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.An OUTFIL

statement contains a HEADER or TRAILER parameter which con-

overlapping fields. This may be caused, for example, by a positional

-parameter specification which overlaps a previously defined field.

ANO DD NAME IN MODS FIELD

: A DD name is missing on the MODS control statement.

ASEP. LKED NOT ALLOWED

A

A

A

IEXPLANATION: A module for which separate link-editing was specified ona MODS control statement is not allowed to be link-edited separately.TASK CALL PARAM ERROREXPLANATION: If a 24-bit list is being used, either a control statementaddress is zero, or the length of a chttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aontrol statement is not positive, or theparameter list ends with the first word of a two-word parameter. If a 31-bitlist is being used, the last parameter word in the list is not followed by thefour byte field X'FFFFFFFF'.INVALID INTERMEDIATE STORAGE DEVICEEXPLANATION: An invalid device was assigned as intermediate storage.Valid devices include IBM's 2305, 2314, 3330, 3330-11, 3340, 3344, 3350,3375, 3380, 3390, and 9345 mass storage system, and equivalent units. Atape device may not be used unless Tape Sort is installed.IMPROPER RETURN CODE FROM ExxEXPLANATION: An invalid return code was passed by the exit that appearsin the message. Valid return codes are 0, 4, 8, 12, 16 (and 20, if the exit isa COBOL or C E15 or E35).[ESTIMATED] PREALLOCATED/USED SORTWORK SPACE USAGE

=,&lt;,&gt;nn.nn

: nn.nn represents the quotient obtained by dividing the

of tracks assigned within preallocated sorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aworks (sortworks allo-

in the JCL or dynamically allocated by an invoking program) by the

of tracks actually used by SyncSort. The word ESTIMATED is in-

in when SyncSort's derivation of this factor is inexact, for example,

all sortwork data sets are not opened, or when data spaces or

are used to contain part or all of the sortwork data.

that for MAXSORTs, the factor displayed is at or near &quot;1.00&quot; for all but

last sort. For the last sort, the factor may be anywhere between &quot;0.01&quot;

&quot;1.00&quot; depending on the amount of data sorted.

15. Messages15.13

WER125ANO DATA ON MODS CARD

: The MODS control statement contains no parameters.

AINVALID CARD BEFORE END CARD

: A control statement containing an error was found.

AI/O ERRORhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a ON SYSIN

: An I/O error occurred on SYSIN.

IPARM FIELD ERROR - xxxxxxxx

: The characters in the message are not a valid PARM.

ignored the remainder of the PARM and continued processing.If

characters appear in the message, then the invalid characters were in

$ORTPARM and are written to SYSOUT and marked with an asterisk.

AExx USER EXIT RETURNED CODE TERMINATE

: Return code 16 was passed by the exit routine shown in the

. SyncSort terminated.

ATASK CALL/E35 TERMINATED PREMATURELY

: An E35 exit routine (COBOL Output Procedure) passed a

code of 8, terminating the sort before the sort was able to pass all of

records. A SORTOUT data set was not present.

ITASK CALL/E35 TERMINATED PREMATURELY

: An E35 exit routine (COBOL Output http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aProcedure) passed a

code of 8, terminating the sort before the sort was able to pass all of

records. A SORTOUT data set was not present.

message may not indicate an error condition - it depends on what the

intended. For example, this message will be generated if a

program using the SORT verb RELEASEs 100 records in the Input

without RETURNing all 100 records in the Output Procedure be-

the logic dropped to the bottom of the Output Procedure &quot;prematurely&quot;.

this is what the programmer intended, then no data has been lost.If,

, the programmer intended the Output Procedure to write all the

read in the Input Procedure, then this message indicates a logic bug

the COBOL program.

AINREC,OUTREC,ddname OUTREC HAS OVERLAPPING FIELDS

: The http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acolumn specification of a c:sub-parameter in the in-

control statement overlaps a field previously defined in the same

statement. Note that the sub-parameters used to define each field

be coded in the order in which the fields will appear in the reformatted

.The ddname will be SORTOUT, SORTOFxx, SORTOFx or the

provided by an OUTFIL FNAMES parameter.

.14 Programmer'sGuide

WER138Addname BLKSIZE NOT EVENLY DIVISIBLE BY LRECL

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.A block was read from the indicated file whose length was not

multiple of the LRECL value, or the JCL or data set attributes are incor-

.

Addname RECFM IS U

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aOFx or the ddname provided by an OUTFIL FNAMES

.SyncSort does not support undefined record format for any of

files.

AMIXED SORTIN TYPES F/V NOT SUPPORTED

: SyncSort permits only one record format type (fixed or

) for input files per sort/merge.

ASORTIN LRECLS ARE MIXED

: The LRECL must be the same for all fixed length files

to a merge.

BUNEXPECTED VIRTUAL STORAGE FRAGMENTATION

: The amount of virtual storage calculated by SyncSort for

2 or 3 was not available in a contiguous block. Additional virtual

was obtained to satisfy the sort requirement. This condition was

caused by virtual storage not released by the user program in the

step (for example, user exit buffer space was not released).

Bnnn BYTES OF EMERGENCY Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPACE

: The indicated amount of virtual storage has been set aside

SyncSort for use by other programs (e.g., program invoking the sort, sys-

SVCs, tape management system).

ICONTROL FIELD GT REC LEN, POSSIBLE OUT OF SEQ REC

: The sort encountered a variable length record that was too

to contain all of the control field(s) specified in the SORT statement.

instructed SyncSort to pad the record with binary zeros to the

of the sort key and continue processing. The added binary zeros ac-

for the position of this record in the sorted file, which may appear to

out of sequence for this reason. The binary zeros are removed when the

is processed for output. Program HISTOGRM may be used to deter-

the length of the shortest record in the input file.

AOPEN ERR SYSIN

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aLANATION: SYSIN is either not present or cannot be opened.

15. Messages15.15

WER149BFRAGMENTED VIRTUAL STORAGE IN SORT PHASE

: The virtual storage specified for SyncSort's use was not

in a contiguous block for Phase 1. This condition was probably

by a calling program or user exit routine. SyncSort obtained its vir-

storage in fragments and continued execution. Note that the calling

or user exit routine used virtual storage in such a way as to cause

, which might another time result in ABEND 80A or S804.

BSECONDARY EXTENTS OBTAINED xxx

: This gives the number of secondary extents obtained for

data sets.

BREQUESTED VIRTUAL STORAGE NOT AVAILABLE, nnn BYTES

: The CORE parameter specified a value which was not

whehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1an SyncSort received control. The number of available bytes

by SyncSort is given.

AINSUFFICIENT VIRTUAL STORAGE IN INT.,FINAL MERGE

: The amount of virtual storage available for the indicated

phase (the intermediate or final merge phase) was not sufficient to

execution. Refer to the &quot;Setting CORE&quot; section of the Performance

chapter for further information.

ANO MODS DD CARD

: The DD statement whose name was specified on the MODS

statement was not provided, so the user exit routine cannot be found.

ASPANNED REC. LEN LARGER THAN LRECL/L2

: A record from a VBS SORTIN data set contains a record

than the maximum record length specified by LRECL in the DCB.

: Execute program HISTOGRM to get the length of the longest re-://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ain the data set. Use this length for the LRECL value in the DCB pa-

of the SORTIN data set.

IREC. LEN GT L2, CUT TO L2

: A variable length record read from the SORTIN data set

longer than the maximum record length specified by either LRECL in the

or the l2 value in the RECORD control statement.(If l2 was not speci-

, the variable length record is longer than the l1 value.)SyncSort has

the record.

: If truncation is not desired, execute program HISTOGRM to get

length of the longest record in the data set. Use this length for the

value in the DCB parameter of the SORTIN data set.

.16 Programmer'sGuide

WER159AREC LEN 0, SORTIN REC x, INSERTED REC x

: A bad variable length record (length code &lt; 4 in its Record

Word) has been found. If the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arecord was found in the SORTIN file,

number of the bad record is given. If the record was inserted from a user

exit routine, the number of the inserted record is given. (E.g., 45 indi-

the forty-fifth record read from or inserted into the SORTIN file.)

AREC. LEN GT LRECL/L2, USER REQ ABORT

B

BEXPLANATION: VLTEST has requested the sort to abort because of thefollowing condition. A variable length record read from the SORTIN file islonger than the maximum record length specified by LRECL in the DCB or(after E15 processing) is longer than the l2 value in the RECORD controlstatement.(If l2 was not specified, the l1 value was used as its default.)ACTION: Change the LRECL or l2 value to reflect the record length, orspecify another value for VLTEST. Program HISTOGRM may be used todetermine the length of the longest record in the input file.ALTERNATE PARM USEDEXPLAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aNATION: The alternate PARM option ($ORTPARM DD, PARMEXITor PARMTABLE) was used and SyncSort received the parameters specified.ppp PREALLOCATED SORTWORK TRACKS, ddd DYNAMICALLY

sss ACQUIRED IN xxx SECONDARY EXTENTS, rrr

, TOTAL OF uuu TRACKS USED

: ppp is the number of tracks found available in sortwork

sets which were allocated prior to SyncSort's gaining control. (These

have been allocated in the JCL or dynamically allocated by an invoking

.) ddd is the number of tracks dynamically allocated as primary

by SyncSort. sss is the number of tracks acquired as secondary space,

both preallocated data sets and data sets dynamically allocated by

. xxx is the total number of secondary extents acquired. rrr is the

number of unneeded tracks released from both preallocated data sets

data sets dynahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1amically allocated by SyncSort. uuu is the total number

tracks actually used in sorting.

following notes apply to the information in this message:

ppp may not represent all of the preallocated tracks available, since not

preallocated sortwork data sets may be opened by SyncSort.

uuu may be less than the sum of ppp, ddd and sss since it represents the

actually used and not the space available.

For MAXSORTs, all dynamic allocation and secondary space acquisition

done during the first sort. For this reason, the WER162B message for

first sort will indicate the number of tracks dynamically allocated,

number acquired via secondary extents, etc. However, the WER162B

in all subsequent MAXSORT sorts will report these tracks as

&quot;preallocated.&quot;

15. Messages15.17

WER164Bwww BYTES OF VIRTUALhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a STORAGE AVAILABLE, xxx BYTES RE-

, yyy BYTES RESERVE REQUESTED, zzz BYTES USED

: The amount of virtual storage available (free) when

received control is represented by www. The amount of virtual

requested for SyncSort's use is represented by xxx. The amount of

storage that the user requested SyncSort to reserve below the

-megabyte line is represented by yyy.The amount of virtual storage used

SyncSort is represented by zzz.This message reflects the total amount

virtual storage below and above the 16-megabyte line that was available

SyncSort and used by SyncSort.

ISTAT DATA REC NOT WRITTEN

: The installation default for the SyncSort SMF record fea-

is applied, but the sort did not invoke the module that creates the sort

record. A possible reason for the sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at's not invoking the module

be that FREE=CLOSE was coded on the SORTOUT (SYSUT2) or

DD statement.

: Remove the FREE=CLOSE parameter if full SMF statistics are

.

LEN GT L3, CUT TO L3

: SyncSort has truncated a variable length record prior to

processing. If an E35 exit was in use, the truncated record was longer

the LRECL of the output file's DCB or greater than the l3 value on the

control statement. If an E35 exit was not in use, the truncated

was longer than the LRECL in the output file's DCB. If OUTFIL

is requested additional truncation may occur as a result of the

processing regardless of the action requested by the VLTEST

.WER166I

AREC LEN GT L3, USER REQ ABORT

:Prior to output processing SyncSort has encountered a

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arvariable length record longer than the l3 value on the RECORD control

(if an E35 exit was in use) or longer than the LRECL in the output

's DCB.The VLTEST PARM requested SyncSort to terminate when this

occurs.

: Change the LRECL in the output file's DCB or the l3 value on the

control statement (if an E35 exit is used) to reflect the correct re-

length, or specify another value for the VLTEST PARM.

ACONTROL FIELD WITHIN RDW

:A SORT/MERGE control field for a variable length file fell

the Record Descriptor Word of each record. This is a critical error

the control field is specified with a ZD or PD format code.

.18 Programmer'sGuide

WER168ICONTROL FIELD WITHIN RDW

: A SORT/MERGE control field for a variable length file falls

the Record Descriphttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ator Word of each record. (The first byte of the data

of a variable length record is at byte position 5.)

r.ll BATCH nnnn TPF LEVEL tt

: Details on the release level, the batch number and the last

applied to SyncSort are given.WER169I

ACONCAT DS, BLKSIZE NOT DIVIS BY LRECL

A

A

A

A

A

AEXPLANATION: One of the files concatenated to a fixed length SORTINdata set has a BLKSIZE that is not evenly divisible by the original LRECL.ACTION: Check the BLKSIZE specified on each of the DD statements con-catenated to SORTIN.CONCAT DS, LRECLS NE OR RECFMS DIFFEXPLANATION: One of the files concatenated to a fixed length SORTINdata set has an LRECL not equal to the original LRECL; or one of the filesconcatenated to a variable length SORTIN data set has an LRECL greaterthan the original LRECL; or one of http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1athe files concatenated to a fixed or vari-able length SORTIN data set has a RECFM not equal to the originalRECFM. CONCAT DS, BLKSIZE GT ORIG BLKSIZEEXPLANATION: One of the files concatenated to a SORTIN data set has aBLKSIZE greater than the original BLKSIZE.BDWINVALIDEXPLANATION: The Block Descriptor Word of a block in the SORTIN dataset contains a value less than 8; or the Block Descriptor Word contains avalue greater than the number of bytes actually read.ACTION: Check the data set for the invalid block.RDW INVALID, OVERFLOWS BUFFEREXPLANATION: The Record Descriptor Word of a record in the SORTINdata set is too large. (According to the RDW, the record extends beyond thebuffer.)ACTION: Execute HISTOGRM to check the data set for an invalid record.INCORE SORT CAPACITY EXCEEDEDEXPLANATION: There are too many input records to fit in virtual storage.ACTION: Either increase the amount of virtual storage the sort is able touse or supplyhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a SORTWKnn DD statements. (The DYNALLOC option may beused instead of SORTWKnn DD statements.)USER EXIT LKED FAILED

: Exit routine(s) needing to be link-edited were present, but

linkage editor passed a return code greater than 0.

15. Messages15.19

ACTION: Check that the DD statement specified on the MODS control

is present in the JCL and contains the modules specified on the

statement. Check that all exits (except E11, E21, and E31) to be

-edited together have an external name identical to the exit name. Ex-

the linkage editor output for other errors.

ITURNAROUND SORT PERFORMED

: SyncSort was able to sort the input file without using

storage (SORTWKnn's). All input data was contained in virtual

.

ASORTIN [nnnnn] MEMBER NOT FOUND

: A SOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aRTIN DD statement specified a member of a parti-

data set that could not be found.If a value nnnnn is provided, it re-

the concatenation number of the SORTIN data set that has the

-not-found condition.

: Check the SORTIN DD statement for an error or list the members

the partitioned data set.

Addname INVALID DCB PARAMETERS

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.SyncSort is unable to derive RECFM, LRECL, and BLKSIZE

from the JCL, the DSCB on the disk or the tape label.

: Check the JCL and the disk or tape labels for the error.

Addname MEMBER NOT SPECIFIED

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The indicated

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a statement defines a partitioned data set, but a member name has not

specified.

: Specify a member name on the indicated DD statement or change

partitioned data set to a sequential data set.

AINVALID RDW SORTIN,SORTINXX BLOCK x

: An invalid spanned record indicator was detected in a

file whose RECFM=VBS, or an invalid record length was detected

a copy operation.The block number of the file is given and SORTINXX

a merge.

: Execute HISTOGRM to check the data set for a record containing

span bits.

ASORTWORK DATASET REQUIRED

: SORTWKnn data set(s) are required for one of the follow-

conditions in this execution of SyncSort: (1) INCORE=OFF is specified

a PARM, (2) exit E14 or E16 is activated, (3) the SUM control statement

used, (4) the OUThttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aREC control statement is used, (5) the checkpoint-restart

is used, (6) SORTOUT is a VSAM data set, (7) the OUTFIL control

is used.(All conditions only apply to sort applications.)

.20 Programmer'sGuide

WER184AINVALID RETURN CODE FROM E32

I

I

A

A

A

AEXPLANATION: The return code from merge exit E32 must be 8, 12, or 16.SORTIN DCBBLK GT ACTUAL, I/O INEFFEXPLANATION: The I/O rate is reduced to an inefficient level because theblocksize specified for the SORTIN data set is larger than the actualblocksize, causing excessive error correction.ACTION: Correct the blocksize specification for future jobs.SVC nnn IS INCORRECT VERSION OR NON-SYNCSORT - SVC NOTUSED - INEFFICIENT SORTEXPLANATION: The SVC did not return a code indicating it was at thecorrect version level, therefore it was not used.The SVC is either at thhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aewrong SyncSort release/maintenance level or is not a SyncSort SVC. Theproblem could cause less efficient I/O and/or loss of SMF records.ACTION: Notify your system programmer, who should check that the SVChas been installed in the system libraries, has been IPLed into the system,was specified via SYNCMAC, and was not incorrectly overridden via$ORTPARM or the PARM field.ddname CINV SIZE LT RECORD LENGTH BUT SPANNING NOTSPECIFIEDEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.The recordlength is greater than the control interval size specified in the definition ofthe indicated VSAM data set, but the data set definition did not also includea specification for spanned records.ddname IS D.A./DSCB NOT FOUND/OBTAIN FAILEDEXPLANATION: The ddname is either SORTIN or SORTINnn. SyncSortwas unable to successfully issue an OBTAIN for the specified direct accessdata set and was therefhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aore unable to determine the DCB characteristics forthe file. The OBTAIN failed either because the volume parameter was in-correctly specified for the output file indicated or because the data set wasdeleted from the volume. (NOTE:the data set may still be in the mastercatalog even though the data set is no longer on the volume.)ddname DCB RECFM REQUIREDEXPLANATION: The ddname is either SORTIN or SORTINnn.TheRECFM was not specified on the indicated DD statement, nor was it avail-able in the DSCB on disk nor the tape label, and the TYPE operand was notspecified on the RECORD control statement.ddname DUPLICATE OUTFIL SPECIFICATION

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The indicated

file is referred to more than once in FILES or FNAMES parameters

the OUTFIL control statement.

15. Messages15.21

WER191Addhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aname BLKSIZE/LRECL INVALID

: The ddname is either SORTIN or SORTINnn. This mes-

is displayed in conjunction with either WER108I or WER109I which

indicate the invalid DCB characteristic specification. BLKSIZE and

must be equal if RECFM=F. BLKSIZE must be evenly divisible by

if RECFM=FB. BLKSIZE must be greater than or equal to LRECL

4 if RECFM=V.

Addname DCB LRECL MISSING

: The ddname is either SORTIN or SORTINnn. The LRECL

not specified on the indicated DD statement, in the DSCB on the disk,

the tape label, or on the RECORD control statement.

Addname DCB LRECL AND BLKSIZE MISSING

: The ddname is either SORTIN or SORTINnn. The

or LRECL must be specified either on the indicated DD statement,

the DSCB on the disk, or in the tape label.Alternatively, an http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1al1 specifica-

may be included on the RECORD control statement. None of these

were made.

ASORTOUT DCB REQRD/TAPE NOT SL

: DISP=OLD was specified on the SORTOUT DD statement,

tape label was not specified as SL in the LABEL parameter, and required

information (LRECL, RECFM, BLKSIZE) was not specified.

Addname DCB REQUIRED/VSAM SORTIN

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The indicated

file requires additional DCB information (RECFM, LRECL or

) on its DD statement.

Addname RECFM=VB, LRECL GT BLKSIZE

: The ddname is either SORTIN or SORTINnn.

=VB requires the BLKSIZE to be greater than or equal to LRECL

.

Addname RECFM=F/FB, LRECL/BLKSIZE INVALID

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aTION:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.BLKSIZE and

were not equal on the indicated DD statement for RECFM=F, or

was not a multiple of LRECL for RECFM=FB.

Addname VARIABLE LRECL LE 4

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.The LRECL specification on the indicated DD statement did not

4 bytes for the RDW plus 1 byte for data.

.22 Programmer'sGuide

WER199A ddname RECORD TYPE=V, BLKSIZE LE 8

:The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.The BLKSIZE specified for the indicated DD statement did not

4 bytes for the BDW, 4 bytes for the RDW plus 1 byte of data.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aR200Addname RECFM=V/VB LRECL/BLKSIZE INVALID

A

A

A

I

IEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.RECFM=Vor VB requires the BLKSIZE to be greater than or equal to LRECL   4.ddname is D.A./DSCB NOT FOUND/OBTAIN FAILEDEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.SyncSort wasunable to successfully issue an OBTAIN for the specified direct access dataset, and was therefore unable to determine the DCB characteristics of theindicated file. The OBTAIN failed either because the volume parameter wasincorrectly specified for the indicated output file, or because the data set wasdeleted from the volume. (NOTE: the data set name may still be in themaster catalog even though the data set is no longer on the volume.)ddname RECFM INCOMPATIBLE WITH SORTINEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.The recordformats for the input and output files are not the same. (Both formats mustbe either fixed length or variable length.) If you want to convert a variablelength input file into a fixed length output file, use the CONVERT parameterof the OUTFIL or OUTREC control statements.INVALID PAGEFIX SVC NUMBEREXPLANATION: SyncSort's EXCPVR facility is in use but no page-fix SVCnumber was specified at installation time.ACTION: Inform your systems programmer of this error condition.SORTCKPT DD STATEMENT MISSING OR INVALIDEXPLANATION: SyncSort could not take checkpoints because a SORTCKPTDD statement was not supplied or the statement specified an invalid devicefor a checkpoint data set. Invalid devices include DUMMY data sets or de-vices other than disk or tape.Processing continued but checkpoints werenot taken.MIXTURE OF SORTWK DEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aVICES

: SORTWKnn data sets were assigned to different device

.

15. Messages15.23

WER209Bxxx PRIMARY AND yyy SECONDARY SORTOUT TRACKS ALLO-

, zzz USED

: It was necessary for SyncSort to request one or more sec-

allocations for SORTOUT.xxx is the number of tracks that were

allocated, yyy is the total number of tracks acquired via secondary

, and zzz is the total number of tracks actually required to contain

SORTOUT data set.

IE15 RC INVALID, IGNORED

: A return code of 0 or 4 was passed by an E15 exit routine

a time when these return codes are invalid because SyncSort has not

the E15 a record address. The invalid return code was ignored by

, and a return code of 8 was presumed.

B/I [] CALLED BY SYNCSORT; RC=xxxx://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1apar:The sort statistics routine (the name inserted in the mes-

) is called by SyncSort. RC gives the code returned to SyncSort by the

routine. If RC does not equal zero, see &quot;What to Do Before Calling

Product Services&quot; in this chapter.

AILLEGAL SUM DATA FIELD

: A field with an illegal data length was specified on the

statement.

: Correct the field length.

A[SORTOFnn] INREC,OUTREC ARITHMETIC OVERFLOW

: When using either INREC, OUTREC or OUTFIL

, an arithmetic calculation or a data format conversion had an

.An arithmetic calculation overflow will occur if any intermediate

exceeds 15 decimal digits or if division by zero is attempted.Overflow

also occur when converting a number with a value of 4G or more to BI

or a numhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aber with an absolute value of 2G or more to FI format.

: Review the arithmetic calculations specified in the indicated

for errors.If they appear to be correct, consider whether the data

possibly cause an overflow or division by zero.If possible, eliminate

data with questionable values via INCLUDE/OMIT.Consider changing

order of the calculations to prevent intermediate calculation overflow.

ASUM FIELD OUTSIDE RANGE

: A sum field on the SUM control statement is located be-

the record length.

ADYNALLOC UNIT,STORCLASS ASSIGNMENT ERROR

: Either the unit name or storage class name (DFSMS

) is missing or specified incorrectly.

.24 Programmer'sGuide

WER218ADYNALLOC WORKFILE ASSIGNMENT ERROR

: More than 32 work files were requested for dynamic allo-://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar.

ADYNALLOC FAILED RC=(nnnn) - uuuuuuuu

I

A

AEXPLANATION: The execution of the DYNALLOC macro instruction failed.nnnn represents the error reason code, and uuuuuuuu represents either theunit name or storage class name.Two possible reason codes are:021C - Undefined unit name.0214 - Unit not available. If all specified units are unavailable whenDYNALLOC is issued, the DYNALLOC request fails.For other reason codes, see either IBM publication MVS/Extended Archi-tecture System Programming Library: System Macros and Facilities,GC28-1150 or MVS/ESA System Programming Library: Application Devel-opment Guide, GC28-1852.DYNALLOC FAILED RC=(nnnn) - uuuuuuuu SORT PROCESSINGCONTINUESEXPLANATION: Dynamic allocation was unsuccessful. uuuuuuuu repres-ents the unit name or storage class name, and nnnn represents the errorreason code. Sort processing continues with previously allocated Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aORTWKsand JCL-allocated SORTWKs.For an explanation of the error reason code,see either IBM publication MVS/Extended Architecture System Program-ming Library: System Macros and Facilities, GC28-1150, or MVS/ESA Sys-tem Programming Library: Application Development Guide, GC28-1852.ILLEGAL OVERLAPPING OF SUM FIELDSEXPLANATION: A SUM field overlaps another SUM field, a SORT/MERGEcontrol field or the Record Descriptor Word of a variable length record. Allof these are illegal.ddname ASCII XLATION, BUT VOLUME IS NOT ASCII TAPE OR

IS V

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.RECFM=D was specified for the indicated file which is not a

data set. (RECFM=D is valid for tape data sets only.)Or, RECFM=D

specified for the input data set and no DCB was specified for the output

set.

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aACTION: In the first case, code correct RECFM for the data set specified; in

latter case, code DCB characteristics for the output data set, and rerun

job.

15. Messages15.25

WER224Addname NOT DEFINED

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.A required input or output DD statement could not be found.

IE35 RC INVALID, IGNORED

: An invalid return code was received from an E35 exit rou-

. If an output data set was not present, the invalid code was other than

or 8, and SyncSort assumed return code 4. If end of file was reached, the

code was other than 8 or 12, and SyncSort assumed return code 8.

Addname BLKSIZE GT ASCII LIMIT

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the dhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1adname provided by an OUTFIL FNAMES parameter.The DD

for an output data set targeted to an ASCII-labeled tape requested

blocksize greater than 2048 bytes; that violates the standard and cannot

done.

Addname DCB BLKSIZE GT TRACK CAPACITY

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The BLKSIZE

the indicated output file was greater than the track capacity of the output

.

: Specifying the track-overflow RECFM in the DCB may possibly

the error condition, or the BLKSIZE should be reduced.

Addname DSORG NOT PS/PO

: The ddname is either SORTIN, SORTINnn, SORTOUT,

, SORTOFx or the ddname provided by an OUTFIL FNAMES

.This ddname must be a sequential data set (PS) or a partitioned

set (PO) mhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aember.

A[ddname] xxxxxxxx FIELD OUTSIDE RANGE

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.A field speci-

in the SORT/MERGE statement is not located within the first 4088

of the variable length record.(This limit is lower if AC, AQ, E, PD0,

x or LOCALE CH fields are used.)Alternatively, a field specified for

, OUTREC, OUTFIL OUTREC, SECTION control, (SUB)TOTAL,

(SUB)MIN, (SUB)MAX, (SUB)AVG or HEADER/TRAILER data field is lo-

beyond the maximum record length. Or INREC, OUTREC, OUTFIL

or HEADER/TRAILER n/col/date/page attempted to build a record

than the allowable maximum.

A[ddname] INREC,OUTREC - ILLEGAL DATA FIELD

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES paramehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ater.An error was

in the INREC, OUTREC or OUTFIL OUTREC specification.

.26 Programmer'sGuide

ACTION: Check the statement for alphabetic data in a numeric field, for a

value of 0, for an omitted value, for a space value greater than

X, for incorrect boundary alignment, and for inclusion of the &quot;variable

&quot; of fixed length input records in the output records.Also,

=ANSI or LINES=(ANSI,n) may not be used on the OUTFIL state-

when using multi-line OUTREC.

Addname RECFM=VBS, LRECL MISSING

A

I

A

A

I

IEXPLANATION: The ddname is either SORTIN or SORTINnn. A RECFMof VBS was specified without an accompanying LRECL specification.VIO INVALID FOR DYNALLOCEXPLANATION: VIO is not permitted as a unit device for dynamic allo-cation. This is due to a possiblhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ae performance degradation if VIO data setsare used as SORTWK.DYNALLOC REQUEST FOR GT 32 SORTWKSEXPLANATION: A total of more than 32 work files were specified in boththe JCL and the DYNALLOC parameter combined. The number was reducedto 32.[ddname] INREC,OUTREC RDW NOT INCLUDEDEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.Four bytesmust be provided for the RDW of the variable length output record in theFIELDS parameter of the INREC, OUTREC or OUTFIL OUTREC specifi-cation. These bytes must appear at the beginning of the record and must notbe edited.[ddname] INREC,OUTREC NULL RECORDEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.A variablelength INREC, OUTREC or OUTFIL OUTREC output record must containat least one data byte from the &quot;fixed portion&quot; of the input record in additionto the RDW.Or if muhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1alti-line OUTFIL OUTREC is being used, at least onenon-blank line must be defined.OUTREC RECORD LENGTH=xxxxEXPLANATION: The xxxx represents the length of the record after OUTRECprocessing. OUTREC occurs prior to E35 and/or SORTOUT/OUTFIL proc-essing. If the data consists of variable length records, xxxx represents themaximum record length.POTENTIALLY INEFFICIENT USE OF INREC

: The INREC control has been used to lengthen the input

length.This can reduce SyncSort performance because a larger vol-

of data is being processed than if the OUTREC control statement were

to perform the same function.Typically, increasing the record length

15. Messages15.27

with INREC is only useful when expanding SUM fields with leading zeros

prevent an overflow condition during SUM.

: Revise the application so that addition of data is performed in an

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arOUTREC statement. Be sure to adjust the FIELDS of the SORT, MERGE

SUM control statements if necessary.

ATYPE PARAMETER REQUIRED

: There was a VSAM input or output file but the TYPE pa-

was not specified. Or, an E15 or E32 exit routine is passing all of

records to the sort/merge (no SORTIN/SORTINnn), but the TYPE pa-

was not specified on the RECORD control statement.

Addname UNSUPPORTED DCB FUNCTION

: The DD statement specified or implied an attribute which

not supported, e.g., hardware keys for a disk output data set or a block

length other than 0, 4 or L for an ASCII tape output data set.

ISHORT RECORD FOR SUM

: One or more variable length records were too short to

all the sum fields specified on the SUM control statement. These

were thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aherefore not summarized. Program HISTOGRM may be used

determine the length of the shortest record in the input file.

A [ddname]INREC,OUTRECSHORTRECORD

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.A variable

record was too short to contain all the fields specified on the control

.Program HISTOGRM may be used to determine the length of the

record in the input file.

I FILESIZEx

: The number of bytes of input data sorted or copied by

is given for FILESIZE.This number reflects SORTIN, E15,

/OMIT and INREC processing.Note the following:

.For MAXSORT, the FILESIZE is given in kilobytes for each individual

in a WER351I message; the FILESIZE in the WER246I for the final

is the sum of the individual shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aorts' sizes and, because of truncation

each intermediate sort, may not be exact.

WER246I is issued instead of WER054I in a variable length re-

copy operation, the number of bytes processed (copied) includes

segment descriptor words for a single record if the record is

of multiple segments on SORTIN, since all segments were

; for a variable length record sort or merge operation, the number

bytes processed (sorted or merged) includes a single record descriptor

for each record even if the record is comprised of multiple segments

SORTIN, since it is records, not record segments, that are being op-

on.2.

.28 Programmer'sGuide

WER247Addname HAS INCOMPATIBLE LRECL

A

A

A

A

AEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor thttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ahe ddname provided by an OUTFIL FNAMES parameter.There is aconflict between the LRECL specification for the indicated output file andeither the post-OUTFIL or post-OUTREC record length. Padding of recordsis not permitted after OUTFIL processing, so the LRECL may not be greaterthan the post-OUTFIL record length. Alternately, truncation of records isnot permitted after the OUTREC statement or the OUTFIL OUTREC proc-essing, so the LRECL may not be less than the post-OUTREC record length.[ddname] INCLUDE/OMIT FIELD BEYOND RECORDEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.A comparefield specified for INCLUDE, OMIT or OUTFIL INCLUDE/OMIT extendedbeyond the end of the record.xxxx INVALID yyyyyyyyyyEXPLANATION: The xxxx represents either INCL (INCLUDE) or OMIT.The invalid relational condition represented by yyyyyyyyyy was found in theINCLUDE or OMIT specification.INCLUDE/OMIhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aT FORMATS INCOMPATIBLEEXPLANATION: A relational condition specified on an INCLUDE or OMITcontrol statement or OUTFIL parameter contains an invalid field-to-field,field-to-constant or field-to-mask comparison.Note that if LOCALE proc-essing has been specified, a CH to BI comparison is not supported.ddname VSAM OPEN,CLOSEERROR - xxEXPLANATION: The ddname is either SORTIN, SORTOUT, SORTOFnn,SORTOFn, or the ddname specified on an OUTFIL FNAMES parameter.An error occurred during an attempt to OPEN or CLOSE the indicatedVSAM file.For the definition of the error number xx, consult one of the fol-lowing IBM publications: MVS/XA VSAM Administration: Macro Instruction Reference,CG26-4016 MVS/DFP Macro Instructions for Data Sets, SC26-4747 DFSMS/MVS Macro Instructions for Data Sets, SC26-4913VSAM LOGICAL ERROR xx ON INPUT,OUTPUT

: An error occurred while processing a VSAM data set. For

definition of the hexadehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acimal error number represented by xx, see one

the following IBM publications:

MVS/XA VSAM Administration: Macro Instruction Reference,

-4016

MVS/DFP Macro Instructions for Data Sets, SC26-4747

DFSMS/MVS Macro Instructions for Data Sets, SC26-4913

15. Messages15.29

WER256Iddname VSAM file, RECORDS PADDED ON OUTPUT

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The fixed

VSAM LRECL for the indicated output file is greater than the length

the records at the end of SyncSort processing. SyncSort padded the output

with filler characters on the right.

RECORD LENGTH=xxxxx

: xxxxx represents the length of the record immediately after

processing.If you have variable length records, xxxxx represents the

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1am record length.WER257I

A DUPLICATEDDNAME:SORTINxx

: Two input files for a merge have the same number. The file

is given.

ADUPLICATE ALTSEQ STATEMENT

: Two ALTSEQ control statements were found.

IRECOVERY FROM B37 SUCCESSFUL. SORT PROCESSING CON-

: SyncSort recovered from a B37 abend and continued proc-

.

SORT NOT RESIDENT - INEFFICIENT SORT

: The resident SyncSort load module(s) were loaded into the

area instead of being executed from the Link Pack Area/Extended

Pack Area.This situation may have occurred because the module(s)

found in a STEPLIB/JOBLIB DD data set. Loading the resident mod-

into the private area limits the amount of virtual storage available to

sort and may reduce the efficiency of the sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at.

: Contact the systems programmer in charge of SyncSort installa-

.WER262I

AILLEGAL USE OF MULTI-VOLUME SORTWK

: SyncSort does not support the use of multi-volume disk

data sets. (However, if SyncSort only requires the use of the space

the first volume of a multi-volume SORTWK file, this error message will

be issued.)

: Remove the volume count subparameters of the UNIT parameter

all SORTWK DD statements that specify more than one volume.

AUNEQUAL REC LENS - VSAM SORTIN - TYPE=F

: A record in a fixed-length VSAM input data set was en-

whose length was not equal to the length specified in the RE-

statement or VSAM cluster definition.

: Use the IDCAMS utility to identify and correct the records in er-

.

.30 Programmer'sGuide

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arWER265Addname VSAM CONCATENATED SORTIN NOT ALLOWED

: The ddname indicated represents either a SORTIN or

input file which consists of concatenated VSAM data sets.

does not support concatenated VSAM input files.

AALTPARM - PARM LENGTH GT MAX SUPPORTED

: The length of the parameter list passed through the alter-

parameter data set exceeded the 256 byte limitation.

Astatement STATEMENT:STATEMENT NOT FOUND

A

A

A

A

A

A

A

AEXPLANATION: A required SORT/MERGE or RECORD statement (as in-dicated in the message text) is missing.statement STATEMENT: SYNTAX ERROREXPLANATION: A SyncSort control statement, as indicated in the messagetext, contains a syntax error. The next line will contain an '*' indicating theapproximate location of the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asyntax error.statement STATEMENT:DUPLICATE STATEMENT FOUNDEXPLANATION: More than one SORT/MERGE, INCLUDE/OMIT, INREC,OUTREC, RECORD, MODS, SUM, ALTSEQ or END statement was found,as indicated.statement STATEMENT: DUPLICATE PARM FOUNDEXPLANATION: A single parameter was multiply specified on the indicatedSyncSort control statement; or a single parameter was specified both in theinvoking parameter list and in the control statements.statement STATEMENT: NUMERIC FIELD ERROREXPLANATION: A numeric field has been improperly specified on the indi-cated SyncSort control statement.statement STATEMENT: PARMS NOT FOUNDEXPLANATION: Required parameters have not been included on the indi-cated SyncSort control statement.BLANK STATEMENT FOUNDEXPLANATION: A blank statement has been encountered.CONTINUATION STATEMENT ERROR FOUNDEXPLANATION: SyncSort has encountered a statement containing a con-tinuation indicator, but cannot locate a continuation stathttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aement which shouldfollow.NO KEYWORDS FOUND ON CONTROL STATEMENT

:A required keyword has not been specified on a SyncSort

statement.

15. Messages15.31

WER300ASORTBKPT DD STATEMENT REQUIRED

: The SORTBKPT DD statement was not included in the job

. This is a required data set for all MAXSORTs.

ASORTBKPT DATA MUST RESIDE ON DISK

: The SORTBKPT data set must be allocated to a disk de-

.

ASORTBKPT TRACK CAPACITY TOO SMALL

: Direct access devices with a track capacity smaller than

bytes cannot be used for the SORTBKPT data set.

ASORTBKPT SYSTEM OPEN FAILURE

: The operating system could not open the SORTBKPT data

.

: Check to see that the DD statement is correct. Determine if oper-

system is at proper mahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aintenance level.

ASORTBKPT RECORD FORMAT ERROR

: There is a record format error in the SORTBKPT data set.

: Check that the SORTBKPT DD statement points to the correct

. Check that the data set has not been inadvertently written into

modified. Use the HEX function on the OUTREC statement or OUTREC

on the OUTFIL statement to get a hex format listing of the data.

ASORTBKPT RECORD EXCEEDS BLKSIZE

: The use of an excessive number of parameters in a control

has caused the SORTBKPT data set to overflow the maximum

limit of 32760.

: Reduce the size of the control statement specification if possible,

convert the application from a MAXSORT to a conventional sort.

ARESTART FROM BREAKPOINT PROHIBITED

: The SORTBKPT data set indicates that a prhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aogram-

sort or a sort with exit programs tried to restart from a breakpoint.

: Use MVS checkpoint facilities since only these will save your work

and the program memory for restart.

ASORTBKPT RECORD SEQUENCE ERROR

: An out-of-sequence record was read from the SORTBKPT

set.

: Use the HEX function on the OUTREC statement or OUTREC

on the OUTFIL statement to get a hexadecimal listing of the data

for analysis. See if the data set was damaged by another program. Check

for hardware error.

.32 Programmer'sGuide

WER308ABREAKPOINT ID NOT FOUND ON SORTBKPT

: The parameter RESTART=id was specified but id could not

found.

: Check spelling, correct, and return.

ASORTOUXX DATA MUST BE ON DISK OR TAPE

: Intermediate sorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at output data was allocated to an unsup-

device. Only disk or tape is allowed.

: Allocate SORTOUxx data to either disk or tape.

ASORTOUXX DEVICE MIXING PROHIBITED

A

A

A

A

A

AEXPLANATION: Intermediate sort output was allocated to both tape anddisk in the same job or to a mixture of disk device types.ACTION: Allocate all intermediate sort data to the same device type.DISK SORTOUXX REQUIRES SORTOUXX DDEXPLANATION: No SORTOUxx DD statements were found so there wasno place to store intermediate sort output.ACTION: Supply one or more SORTOUxx DD statements with xx repres-ented by 01 to 99.TAPE SORTOUXX REQUIRES SORTOU00 DDEXPLANATION: One or more SORTOUxx DD statements were allocated totape but the SORTOU00 statement was not present.ACTION: Allocate a tape unit using the SORTOU00 DD statement.SORTOUXX DEVICE NOT SUPPORTEDhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aEXPLANATION: The SORTOUxx DD statements specify an unsupporteddevice type.ACTION: Refer to the list of supported devices for SORTOUxx and changethe allocation to one of these devices.INSUFFICIENT VIRTUAL STORAGE FOR MAXSORTEXPLANATION: MAXSORT cannot run efficiently in the amount of virtualstorage provided.ACTION: Increase virtual storage or decrease the number of tape units re-quested by MINMERGE.SORTOUXX BLKSIZE GT TRACK CAPACITYEXPLANATION:Intermediate sort output is on disk, but the SORTIN dataset requires too large a blocksize for a disk device.ACTION: Allocate intermediate sort output to tape and rerun.INSUFFICIENT SORTOUXX DD STATEMENTS

: The data to be sorted requires one or more additional data

.

: Recalculate and restart the job including additional SORTOUxx

statements. (Make sure each statement's number is greater than the last

you put in.)

15.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Messages15.33

WER317IMAXSORT OPTION SELECTED

: A MAXSORT was requested.

CARDS IGNORED - SORTBKPT USED

: The control statement just listed on SYSOUT for a break-

restart were not used to control sorting. Whatever control statements

specified when the job was started were used. (They may be the same

the statements just listed, however.)

RESTARTED AT BKPT xxxxxxxxxxxx

: This message identifies the breakpoint id from which

resumes execution on a breakpoint restart.

SORTOUXX BLKSIZE FORCED

: Due to the constraints between the amount of memory and

value specified for MAXMERGE, MAXSORT was forced to compromise

choose a smaller blocksize than would permit efficient buffering in sorts

merges.

: If you wish a more efficienthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a MAXSORT, either increase the amount

memory or reduce the number specified for MAXMERGE. This will permit

larger blocksize to be chosen which will allow multiple buffering of all the

sort output data.WER318IWER319IWER320I

B SORTOUXXBLKSIZE=xxxxx

: This gives the blocksize that MAXSORT has chosen for

sort output.

ATAPE DYNALLOC FAILURE - CODE=xxxx

: Attempts to dynamically allocate tape units for a merge

met with unexpected failure. Code xxxx gives the hexadecimal return

from the dynamic allocation request.For an explanation of this code,

either IBM publication MVS/Extended Architecture System Program-

Library: System Macros and Facilities, GC28-1150, or MVS/ESA Sys-

Programming Library: Application Development Guide, GC28-1852.

ABKPT DATA AT http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aDIFFERENT RELEASE LEVEL

: The SORTBKPT data was created by a different SyncSort

than the SyncSort program reading it.Because of this, the break-

data cannot be processed.

: Restart this job and run under the same SyncSort release that you

with.

ATAPENAME CLASS NOT FOUND ON SYSTEM

: The tapes could not be dynamically allocated because a

was specified that was not generated into the operating system.

: Check with the systems programmer for acceptable unit names.

.34 Programmer'sGuide

WER325AMAXSORT STOPPED BY OPERATOR

: The operator responded to a message by stopping the sort.

sort may be restarted from the last breakpoint or checkpoint.

ADYNALLOC UNALLOC FAILURE - CODE=xxxx

A

A

A

A

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aR331A

IEXPLANATION: Attempts to dynamically deallocate tape units met withunexpected failure. Code xxxx gives the hexadecimal return code from thedynamic deallocation request.For an explanation of this code, see eitherIBM publication MVS/Extended Architecture System Programming Library:System Macros and Facilities, GC28-1150, or MVS/ESA System Program-ming Library: Application Development Guide, GC28-1852.INSUFFICIENT UNITS FOR MINIMAL MERGEEXPLANATION: Too few tape units were allocated to meet the numberspecified in MINMERGE. Either too few SORTOUxx DD were supplied orthe MVS system was unable to dynamically allocate enough units.ACTION: Restart the job with additional SORTOUxx DD statements.SORTOUXX SYSTEM OPEN FAILUREEXPLANATION: The operating system could not open the SORTOUxx datasets.ACTION: Check to see that SORTOUxx DD statements are correct. Deter-mine if operating system is at a proper maintenance level.SORTOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aU00 SYSTEM RDJFCB FAILUREEXPLANATION: The operating system could not read the Job File ControlBlock for SyncSort analysis.ACTION: Determine if operating system is at a proper maintenance level.SPECIFIED SORTING TIME HAS EXPIREDEXPLANATION: The time limit specified in the SORTTIME parameter hasexpired. The job may be restarted from the last breakpoint or checkpoint.SYSTEM CHECKPOINT FAILUREEXPLANATION: Request for MVS checkpoint facilities failed.ACTION: Ascertain that the SORTCKPT DD statement was correctly speci-fied. Check that rules for the use of checkpoint were not violated.SORT/MERGE # XX COMPLETE AT BREAKPOINT/AT

bbbbbbbbbbbb, DIAG=hhhh,hhhh...

: This message tells which individual sort or merge has

. Restart can be performed from the breakpoint or checkpoint id

in bbbbbbbbbbbb.If restart is not possible the above message will

:

/MERGEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a # XX COMPLETE.

hexadecimal information following the DIAG keyword is likely to change

execution to execution. It is internal diagnostic information intended

use by SyncSort personnel in Product Support.

15. Messages15.35

WER351IDATA SIZE xxxx KB [FROM yy WAY MERGE]

: The amount of data that was processed for the current

individual sort/merge is given in kilobytes. When a merge is proc-

yy gives the number of tape units used.

ALLOCATED TAPE UNITS - XX

: The number of tapes drives that were dynamically allo-

for the current merge pass is given.

TIME hh.mm.ss - ENDING TIME hh.mm.ss

: The starting and ending times in hours, minutes, and sec-

of the individual sort or merge just completed are given.

----------------------DATA SET Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aTATUS----------------------

: This is a header.Messages relating to data sets will follow.

=dsname

: The data set names of the tapes for intermediate sort out-

are given. Retain these reels for input to a later merge.

SERS = vvvvvv...

: The tape volumes are listed for tape intermediate sort

. Retain these reels for input to a later merge.

DD STATEMENT IS ACTIVE

: The disk data set allocated to the SORTOUxx DD state-

is needed as input to a subsequent merge. Be sure to keep it in case

is necessary.WER352IWER353IWER354IWER355I WER355IWER356I

Djobname.stepname - MAXSORT BKPT id

ESTIMATE: XXX MINUTES UNTIL NEXT NOTIFICATION.

'GO' TO CONTINUE, 'STOP' TO TERMINATE

:A long-running MAXSORT has exhausted its assigned

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ak of computer time.

: The operator's decision should be based on scheduling priorities

the estimated time of the sort. A 'GO' reply will permit sort execution

proceed in stages. This message is generated at discrete intervals so that

operator can again opt to continue or terminate its execution.

Djobname.stepname - MAXSORT BKPT id

TAPE UNITS ALLOCATED TO jobname

TAPE UNITS NEEDED FOR BEST PERFORMANCE

ESTIMATE USING aaa TAPE UNITS -

MINUTES TO  NEXT BREAKPOINT | END OF JOB

'GO' TO CONTINUE, 'STOP' TO TERMINATE, 'NN' # UNITS

: The first time this message is generated, it indicates that

has dynamically allocated the optimum number aaa of tape

up to MAXMERGE. Reissued, this message documents MAXSORT's

.36 Programmer'sGuide

response to the operator's previhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aous reply of 'NN' tape units.'NN' represents

total number of tapes that will be allocated.

: Given a reply of 'NN' tape drives, MAXSORT will attempt to sat-

the operator's request. For 'NN' larger than aaa, MAXSORT will try to

its allocation to 'NN'. (The operator can delay the request for more tape

in order to give other jobs time to free any tape drives they are using.)

above message is reissued and the operator can see how the decision

affect sort execution.

soon as allocations and time estimates are satisfactory, the reply 'GO' will

continued execution using the allocated tape units. If allocation or time

are not satisfactory, the job may be terminated (reply 'STOP') or

new number 'NN' of units may be requested.

Djobname.stepname - MAXSORT BKPT id

TAPE UNITS AVAILhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aABLE

TAPE UNITS ALLOCATED TO jobname

TAPE UNITS NEEDED TO CONTINUE EXECUTION

'RETRY' TO GET UNITS, 'STOP' TO TERMINATE

: MAXSORT cannot immediately acquire enough tape drives

make continued processing worthwhile.

: The operator can wait until other tape drives have been released,

reply 'RETRY'. If enough drives are now available, execution continues.

the above message is repeated.Eventually enough tape drives

available or the operator terminates the job with a 'STOP' response.

INO ADDITIONAL TAPE UNITS EXIST FOR GENERIC CLASS

: All tape units on the system within the TAPENAME class

been allocated.Further DYNALLOC attempts will fail to acquire more

units. Message WER376D or WER377D will follow.

AMINIMUM SORTWK SPACE NOT AVAILABLE://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a: MAXSORT could not obtain enough SORTWK disk space

run.When MAXSORT is executing with larger storage values, SyncSort

need to automatically raise MINWKSP, overriding the specified

value.Therefore, it may erroneously appear that JCL

provided enough space to satisfy MINWKSP when this message

posted.

: Correct SORTWK volume, primary, and secondary allocations.

the job.

AINSUFFICIENT VIRTUAL STORAGE FOR SORTBKPT BUFFER

: MAXSORT was unable to obtain the necessary 3600-byte

space from the operating system.

: Check to see that sufficient virtual storage was allocated to the

.

15. Messages15.37

WER392ASORTBKPT FORMAT ERR - VBS PROCESSING

: MAXSORT attempted to read back control information

with VBS SORTIN dahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ata and found a format error in the

data set.

: In the U.S. and Canada, call SyncSort MVS Product Services di-

at (201) 930-8260. Elsewhere, call your SyncSort support represen-

.

ITURNAROUND MAXSORT SORT PERFORMED

: The amount of SORTIN data was small enough to fit en-

on SORTWK disk space, so sorted data was produced in one SyncSort

.

ASORTOUXX DD STMT REQUIRED FOR MERGE

: The above DD statement was required for disk intermedi-

sort output as input to a merge but could not be found.

: Supply the missing DD statement.

AINVALID SORTOU00 OR SORTOUxx DSN PREFIX

: The BKPTDSN parameter was used, but the required

period was not specified as part of the DSN prefix.

: Add a trailing period to the parameter specificahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ation.

ALKED DD STATEMENT MISSING OR INVALID

: A MODS statement specified at least one exit to be link-

by SyncSort, but a SYSPRINT and/or SYSLIN and/or SYSLMOD DD

is missing. All of these statements are required for link-editing.

, the SYSLMOD DD statement does not refer to a data set on a direct

device.

: Supply the missing DD statement(s) or adjust the SYSLMOD DD

as appropriate.

ASORTIN(nn) IS AN UNINITIALIZED SEQUENTIAL DISK DATA SET

: The data set was allocated but never opened for output.

, there is no valid data or end-of-file mark in the data set. This

usually occurs when a program abends and the steps to create the

are bypassed.

: Write the appropriate data or end-of-file mark in the data set.

ACSECT NAME DIFFEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aRENT THAN MEMBER NAME

: The MODS statement specified an exit routine module in

that was not found.

: Either change the member name in the MODS statement to match

module name or reassemble the exit module with a name to match the

name on the MODS statement.

.38 Programmer'sGuide

WER402ASORTMODS STOW FAILURE

A

I

I

AEXPLANATION: While copying an exit routine from SYSIN to SORTMODS,SyncSort attempted unsuccessfully to store (STOW) the exit routine in theSORTMODS directory. This condition is caused either by specifying insuffi-cient directory blocks when creating the SORTMODS data set or by thepresence of a member or alias with the same name as the exit routine in theSORTMODS data set, or by a hardware failure.ACTION: Check the SORTMODS directory names for a member-name con-flict and rerun the job sthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aep.OUTFIL NOT VALID FOR MAXSORTEXPLANATION: Using an OUTFIL control statement in a MAXSORT ap-plication is not supported at this time.ACTION: Either remove the OUTFIL statement(s) or convert the applicationnot to invoke MAXSORT.SORTXSUM:RECFM= ;LRECL= ;BLKSIZE=,CISIZE=[;CINVACCESS]; RCD OUT nEXPLANATION:This informational message lists the DCB characteristicsused by SyncSort to process the SORTXSUM file, as well as the number ofrecords (n) that were written to the data set.For a VSAM data set, theCISIZE is provided; if control interval access was used, the CINV ACCESSportion of the message will be displayed.ddname DATA RECORDS OUT n, TOTAL RECORDS OUT yEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.The n re-presents the number of data records (exclusive of HEADERS/TRAILERS andmulti-record OUTREC) in each output data set.The y represents the totalnumber of records in ehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aach output data set (data records,HEADERS/TRAILERS and multi-record OUTREC records).Note that thetotal number of lines written to the line printer may be greater than theactual record count since multiple lines can be generated from one data re-cord using ANSI control characters.ddname HEADER/TRAILER/DATA LINES EXCEED PAGE SIZE

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.The number

lines generated by some HEADER and/or TRAILER and/or multi-line

parameters is greater than or equal to the number of lines to be

per logical page as specified by the LINES parameter. If LINES has

been coded, this number defaults to 60.

: Reduce the number of HEADER/TRAILER lines generated or in-

the number of lines in the LINES parameter so that a minimum of

output lines from 1 data recorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ad can be written per logical page.

15. Messages15.39

WER407IUNUSABLE SORTWK DEVICE ALLOCATED ,NON RPS,UNIT=VIO

: An unusable device was allocated during dynamic allo-

. The device was held for the duration of the sort; however, the device

not used for SORTWK storage.

:For future executions, ensure that the DYNALLOC runtime pa-

specifies a correct disk device.If the message cites &quot;NON RPS,&quot;

RPS disk devices; if the message cites &quot;UNIT=VIO,&quot; specify a true

device.

AMOD ON SYSIN NOT FLAGGED AS SYSIN MODULE

: An object deck was found in the SYSIN data set that, ac-

to the MODS statement, was not specified as belonging in SYSIN.

Bxxx BYTES OF VIRTUAL STORAGE AVAILABLE ABOVE 16MEG

,

BYTES RESERVE REQUESTED, zzz BYTES http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aUSED

:The amount of virtual storage above the 16-megabyte line

(free) when SyncSort received control is represented by xxx. The

of virtual storage that the user requested SyncSort to reserve above

16-megabyte line is represented by yyy.The amount of virtual storage

by SyncSort above the 16-megabyte line is represented by zzz.

Bnnn BYTES OF EMERGENCY SPACE ALLOCATED ABOVE 16MEG

: The indicated amount of virtual storage above the

-megabyte line has been set aside by SyncSort for use by other programs

(e.g., program invoking the sort, system SVCs, tape management system.)

IERROR TAKING SYSTEM CHECKPOINT. PROCESSING CONTIN-

: An error occurred when SyncSort attempted to take a

-requested checkpoint. Sort/merge processing continued; however, a us-

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1able checkpoint may not exist. Refer to the IHJxxxx message in the job log

determine the cause of the error.

ASORTIN(nn) OPEN ERROR ON AN UNINITIALIZED SEQUENTIAL

DATA SET

: An error occurred during an OPEN of a multi-volume un-

sequential disk data set being used for SORTIN(nn).When the

=YES option has been selected, either by default or parameter

, SyncSort will need to open for output a multi-volume uninitialized

data set in order to set the DS1IND80 flag in the format-1 DSCB of the

volume. Typically this error will occur if the SyncSort step does not have

authority to open the SORTIN(nn) for output processing.

:In a separate step prior to the SyncSort invocation, write the ap-

end-of-file mark in the first volume of the multi-volume data set.

.40 Programmehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ar'sGuide

WER415BDSM FACILITY DISABLED

: SyncSort's dynamic storage management feature was not

for this sort execution.

access-method WAS USED FOR ddname   WER416B ddname: EXCP'S=eee [,UNIT=uuuu] [,DEV=dddd] [,CHP=cccccccc][,VOL=vvvvvv]    TOTAL OF xxx EXCP'S ISSUED FOR totalid

: This message provides summary I/O tuning information for

processed by SyncSort. The first form is used when an access method

than EXCP is used for a file. It uses a generic term for the access

(BSAM, HIPERBATCH, etc.) and the file for which it was used. When

is used, the message takes on the second form which has the compo-

parts listed below. Some of these components may or may not be in-

in the message depending on the level of the operating system and the

of the information within Shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ayncSort.

'S=eee&quot;eee&quot; identifies the number of EXCPs issued for the file. For

files such as SORTIN, this is the total EXCPs issued

all concatenated input sets.

&quot;uuuu&quot; is the unit type on which the data set resides. For

that can consist of concatenations or multi-volume data

, the unit type displayed is for the first volume of the first

set.

&quot;dddd&quot; is the device name for the first or only device for the

.

field identifies the channel paths available to the first

only device.

field is displayed for only DASD devices and identifies

volume serial number of the first or only volume for the

.UNIT=uuuuDEV=ddddCHP=ccccccccVOL=vvvvvv

certain types of sorts, SyncSort may dynamically allocate data sets other

SORTWKnn data sets for use in the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asorting process, and this can occur

or not normal dynamic allocation of sortwork data sets is enabled.

used, such data sets are collectively represented in a single WER416B

using a ddname of &quot;SORTWKXX&quot; for the purpose of reporting

issued against them.

the third form of the message, xxx provides a total of the EXCPs issued for

, SORTING, COPYING, or MERGING, as identified by

&quot;totalid.&quot;

15. Messages15.41

WER417AUNEQUAL MAINTENANCE LEVELS: xxxxxxxx,yy,zz

: The load module xxxxxxxx and SyncSort root module

levels do not correspond. yy represents the maintenance level

the xxxxxxxx module; zz represents the maintenance level of the root

.

: Contact the systems programmer in charge of SyncSort mainte-

.

IDATASPAChttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aE(S) AND/OR HIPERSPACE(S) USED

: SyncSort has dynamically chosen to use Data Space or

during the execution of the sort.

ACCELERATOR ACTIVE

: SyncSort's high performance access method was used for

a COBOL file.WER420I

ASORTOUT STOW FAILURE

: When writing to SORTOUT, SyncSort attempted unsuc-

to store (STOW) the SORTOUT PDS member in the SORTOUT

. This condition is caused by specifying insufficient directory blocks

creating the SORTOUT data set.

: Recreate the SORTOUT data set with more directory blocks and

the job step.

IDYNAMIC ALLOCATION RETRY - WAITING FOR SPACE

: The DYNALLOC facility is being used to acquire sortwork

, but there is currently insufficient disk space on the system to satisfy

rehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aquest. SyncSort will wait the prescribed number of minutes as speci-

by the DYNALLOC option and then retry the request.

ALLOCATION RETRY SUCCESSFUL

: The dynamic allocation of sortwork space after a

RETRY attempt was successful. Sort processing continues.WER424I

ACONVERT FEATURE CANNOT BE USED FOR FIXED LENGTH RE-

: The CONVERT parameter of the OUTREC or OUTFIL

has been used incorrectly. CONVERT can be used to convert

length input to fixed length output records only. Also, the record

of an output data set must be fixed length after CONVERT process-

.

ISORT INTERNAL ERROR - RECOVERY ATTEMPT IN PROGRESS

: The presence of this message indicates that an automatic

of the SyncSort execution has been initiated. If the error recovery ishttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

, the SyncSort SYSOUT listing will contain a subsequent set of

representing the complete information about the execution. The

set of messages may be separated from the initial set of listings

.42 Programmer'sGuide

WER427I

I

I

Iby a diagnostic output of significant size. The new listing will contain themessage WER427I.RECOVERY ATTEMPT IN PROGRESSEXPLANATION: The set of SYSOUT messages containing the WER427I willbe from the automatic retry execution. Examine these messages to insurethat it also contains a WER052I message indicating a successful completionof the SyncSort execution. In addition, a successful SyncSort recovery willcomplete with a return code of zero. Even if the WER426I and WER427Imessages are present, this in itself does not constitute a successful recoveryunless zero is returned for the step completion code.If http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aan execution of SyncSort does utilize the recovery facility, whether suc-cessfully or not, the SyncSort MVS Product Services Group should be con-tacted so that the underlying error can be investigated and resolved.CALLER-PROVIDED IDENTIFIER IS &quot;xxxx&quot;EXPLANATION: SyncSort was invoked by another program, and that pro-gram used a 31-bit parameter list where the &quot;call identifier&quot; parameter wasspecified.xxxx is the identifier specified by the calling program.SORT INTERNAL ERROR ON SORTWKnn - RECOVERY ATTEMPTIN PROGRESSEXPLANATION: An internal error occurred while processing the SORTWKdata set indicated by nn. The presence of this message indicates thatSyncSort has initiated automatic error retry logic to correct this error. If therecovery is successful, processing will resume and message WER052I willbe issued when the sort has completed successfully. Absence of the WER052Imessage indicates that SyncSort was unable tohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a recover.ACTION: If an execution of SyncSort does use this recovery facility, whethersuccessfully or not, SyncSort MVS Product Services should be contacted sothat the underlying condition can be investigated and resolved.SORT INTERNAL ERROR ON SORTOUT - RECOVERY ATTEMPT IN

:An internal error occurred while creating the SORTOUT

set. The presence of this message indicates that SyncSort has initiated

error retry logic to correct this error. If the recovery is successful,

will resume and message WER052I will be issued when the sort

completed successfully. Absence of the WER052I message indicates that

was unable to recover.

:If an execution of SyncSort does use this recovery facility, whether

or not, SyncSort MVS Product Services should be contacted so

the underlying condition can be inhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1avestigated and resolved.

15. Messages15.43

WER431ICOPY SUBSTITUTED FOR MULTIPLE OUTFILS

: The SORT or COPY multiple output application (multiple

) has been automatically converted by SyncSort to a single SORT

COPY operation followed by one or more COPY operations.

system resources are available and the output files of a multiple output

have identical specifications, SyncSort will make this type of

to take advantage of system resources to improve the application's

.

ISORT,MERGE FORMAT OPERAND IGNORED

: On either a SORT or MERGE control statement, the for-

of the keys was specified in both the FIELDS and FORMAT parameters.

ignores the FORMAT parameter and uses the individual format

within the FIELD parameter.

FORMAT Ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aPERAND IGNORED

: On a SUM control statement, the sum field format was

in both the FIELDS and FORMAT parameters.SyncSort ignores

FORMAT parameter and uses the individual format specifications within

FIELD parameter.

/OMIT FORMAT OPERAND IGNORED

: On an INCLUDE or OMIT control statement, the field

was specified in both the COND and FORMAT parameters.SyncSort

the FORMAT parameter and uses the individual format specifica-

within the FIELD parameter.WER433IWER434I

ASORTIN(nn) ALLOCATION ERROR ON AN UNINITIALIZED SE-

DISK DATA SET

: An error occurred during the dynamic allocation of a

-volume uninitialized sequential disk data set being used for

(nn). When the UNINTDS=YES option has been selected, either by

or parameter ovehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arride, SyncSort will need to dynamically allocate

open for output a multi-volume uninitialized disk data set in order to

the DS1IND80 flag in the format-1 DSCB of the first volume.

:In a separate step prior to the SyncSort invocation, write the ap-

end-of-file mark in the first volume of the multi-volume data set.

IUNEQUAL MAINTENANCE APPLIED TO GLOBAL DSM AND

LIBRARIES

: The maintenance level of the SyncSort MVS product is in

with the maintenance level of the Global DSM (GDSM) subcompo-

due to the incomplete application of one or more maintenance levels.

.44 Programmer'sGuide

WER437A[ddname] SPLIT INCOMPATIBLE WITH REPORT WRITINGWER438A

A

A

A

A

IEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aby an OUTFIL FNAMES parameter.The SPLITparameter and one or more report writing parameters have been specifiedfor an OUTFIL group.The specified ddname is the first ddname of theOUTFIL group.SPLIT and report writing parameters are incompatible onthe same OUTFIL control statement.Specifically, SPLIT cannot be specifiedon the same OUTFIL statement with HEADERn, TRAILERn, LINES,NODETAIL, and SECTIONS.[ddname] INREC,OUTREC - NONE OF THE FIND-CONSTANTSWAS MATCHED WITH THE CHANGE FIELD (p,l), CONTENTS OFINPUT FIELD IN HEX: xxxxxxxxEXPLANATION:The ddname will be SORTOUT, SORTOFxx, SORTOFxor the ddname provided by an OUTFIL FNAMES parameter.A CHANGEsubparameter on an INREC, OUTREC or OUTFIL OUTREC control state-ment was specified without a NOMATCH option and the input field did notmatch any of the specified find-constants.p,l represents the position andlength of the input field.xxxxxxxx is the hexadecimal representation of theinput field.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aUNSUPPORTED OPERATING SYSTEMEXPLANATION: Only MVS/XA or MVS/ESA operating environments aresupported by SyncSort MVS 3.6 and higher.ERROR IN CALLING LANGUAGE ENVIRONMENT SERVICE, RC =nnnnEXPLANATION: A Language Environment service used to support LOCALEprocessing indicated a critical error in its feedback code. nnnn is the errormessage number representing the feedback code. For an explanation of thiscode, see the IBM publication Debugging Guide and Run-Time Messages,SC26-4829.INVALID CHARACTER IN COMPARE FIELD FOR ACTIVE LOCALEEXPLANATION: INCLUDE/OMIT processing with the LOCALE functionactive detected a character that is not defined in the current locale. The in-valid character could be in a CH field or in a character or hexadecimal con-stant compared to a CH field.INVALID CHARACTER IN CONTROL FIELD FOR ACTIVE LOCALEEXPLANATION: Sort or merge processing with the LOCALE function activedetected a character that is not defined in the http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1acurrent locale. The invalidcharacter is in a CH sort or merge field.LOCALE PROCESSING USED FOR LOCALE nnnnnn

: Indicates that LOCALE processing was in effect.nnnnnn

(up to 32 characters) represents the name of the locale used.

15. Messages15.45

WER445ALOCALE PROCESSING CONFLICT

:LOCALE processing has been used illegally.LOCALE

cannot be used with an E61 exit.The LOCALE specification

be changed on a MAXSORT breakpoint restart.

A[ddname] INCLUDE/OMIT FORMATS INCOMPATIBLE FOR LO-

PROCESSING

:The ddname will be SORTOUT, SORTOFxx, SORTOFx

the ddname provided by an OUTFIL FNAMES parameter.LOCALE

has been requested and a character (CH) to binary (BI) compar-

was specified on an INCLUDE/OMIT statement or OUTFIL

/OMIT parameter. CH to BI comparisonhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as are not supported when

LOCALE processing.

BPHASE 3 VIRTUAL STORAGE REDUCED TO nnn BYTES FOR OP-

PERFORMANCE

: Phase 3 optimization has determined that a reduction in

storage is appropriate for an efficient execution. nnn is the amount

virtual storage used during phase 3.The total bytes used value in mes-

WER164B indicates the virtual storage used during earlier phases of

sort execution.

IY2 FORMAT CENTURY WINDOW IS FROM xxxx TO yyyy

: One of the Y2x data formats has been used for a

/MERGE field, an INCLUDE/OMIT field or an INREC/OUTREC edit

.The starting year is xxxx and the ending year is yyyy for the century

used to process the fields.

GLOBAL DSM SUBSYSTEM ACTIVE

: The SyncSort Global DSM (GDSM) subsystem was active

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1auring the execution of this SyncSort application.

:The PARASORT technique has been used for this exe-

.WER449IWER450I

APARASORT TAPE LABEL ERROR VOL(vvvvvv)

[CONCATENATION 0nnn]

: The tape label on volume vvvvvv does not match the DCB

of the SORTIN data set.This could happen because of

record length, BLKSIZE or recording format.This situation is

caused by overwriting some of the data in a multi-volume data set.

concatenation number indicates where in the SORTIN concatenation the

in error may be found.

.46 Programmer'sGuide

WER452I

APARASORT NOT USED: reasonEXPLANATION:The PARASORT feature has been disabled and the sortwas performed using conventional SORTIN processing.The message indi-cates the reason for this action, which may be any ohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1af the following: AUTOMATIC RETRY DISABLEDAutomatic sort retry must be en-abled for PARASORT to be used.It is required in the event that thecondition identified in WER454A is encountered. CONCATENATED SORTIN DEVICES DIFFERConcatenatedSORTIN devices must be the same device; that is, unit affinity must bespecified. INCOMPATIBLE CONDITIONSThe application may specify ele-ments that cannot be used together.This problem can be caused byunusual sort key types, some feature combinations, or very long sortkeys. INPUT IS NOT TAPEPARASORT requires input from tape devices.Input from any other source is not permitted. INSUFFICIENT TAPE CHANNELSAt least two channel paths mustbe available to the tape drives being used to read the SORTPARn DDs.For a description of a technique to help insure that this requirement issatisfied, see the description of esoteric unit names in the PARASORTchapters of this manual and the SyncSort MVS Installation Guide. NOhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a SORTWORKS AVAILABLEPARASORT requires sortwork space,which must be specified in the JCL or provided dynamically byDYNALLOC. RETRY IN PROGRESSPARASORT failed, but a retry is being at-tempted. SORTIN IS A NULLFILE SORTIN IS ONLY A SINGLE VOLUME DATA SETThe SORTINDD statement for PARASORT must define either a single multi-volumeSORTIN data set or several concatenated tape data sets, which can besingle or multi-volume.One single-volume data set is not permitted. V(B)S DATA SETS NOT ALLOWEDVS and VBS data sets are notcompatible with PARASORT.FOR PARASORT text

:PARASORT failed and the sort application will not exe-

.The message text indicates the condition that caused the failure or the

requirement that was violated:

A SORTPAR2 DD STATEMENT IS REQUIRED

DUPLICATE VOLUMES ON SORTIN DD NOT ALLOWED

EQUALS MAY NOT BE SPECIFIEDIf EQUALS is not specified on

SORT conhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1atrol statement or as a PARM, ensure it is not enabled by

.Pass NOEQUALS to disable EQUALS.

E15 EXITS MAY NOT BE SPECIFIED

MAXSORT MAY NOT BE SPECIFIED

PASSED SORTIN IS INVALID

15. Messages15.47

SEQNUM MAY NOT BE SPECIFIED ON INRECSKIPREC MAY NOT BE SPECIFIEDSORTIN AND SORTOUT MUST BE DIFFERENT DATA SETSSORTIN GDG NOT ALLOWEDSORTIN VOLUME SEQUENCE MAY NOT BE SPECIFIEDThevolume sequence number must be 1, the first volume.The numbercannot be greater than 1.SORTPAR DD STATEMENTS ARE REQUIREDSORTPAR(N)S MUST BE SEQUENTIALLY NUMBEREDSORTPAR1 AND SORTIN DATA SET NAMES MUST BE THESAMESORTPAR1 DISPOSITION MUST BE OLDSORTPAR1 UNIT MUST BE THE SAME AS THE SORTIN UNITSORTPAR1-4 DEVICE TYPES MUST BE THE SAME AS THESORTIN DEVICE TYPEhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aSORTPAR2-4 CANNOT BE THE SAME AS THE SORTIN UNITSORTPAR2-4 and SORTIN DATA SET NAMES MUST BE THESAMESORTPAR2-4 DISPOSITION MUST BE (NEW,KEEP,KEEP)SORTPAR2-4 MUST SPECIFY DEFER ON THE UNIT PARAME-TERSORTPAR2-4 MUST SPECIFY VOL=PRIVATESTOPAFT MAY NOT BE SPECIFIEDTHE DISPOSITION OF SORTIN IS INVALIDSORTIN data sets

not be temporary data sets.They also may not be NEW, passed or

PASS on their JCL definition.

APARASORT SORTIN END OF FILE ENCOUNTERED BEFORE THE

LIST EXHAUSTED

:The SORTIN volume list is supplied from either the cat-

or specific list of volume serial numbers.The volume serial list must

reflect the volumes in the data set. If extra volumes are specified

(as may happen if an old data set is rewritten with less data) this error

will be generated. A volume sequence number may not be specified.

IPAhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aRASORT CHANNEL CONTENTION - SORTPARn NOT USED

:SORTPAR2-4 has no available channel path to send data

than a path that would conflict with a previously defined SORTPARn

.This SORTPARn will not be used during the PARASORT exe-

.This message may occur more than once if there are multiple con-

SORTPARn DD's.

DATA TRUNCATED DUE TO DCB BLKSIZE OVERRIDE

:An extended sequential data set used as input to a sort,

or copy has had its DCB BLKSIZE overridden to a smaller value via

JCL specification.A physical block exceeding this overridden BLKSIZE

was truncated to the smaller size during input processing.WER460I

.48 Programmer'sGuide

ACTION:Confirm that this truncation is desired.BLKSIZE specification from the JCL.

not, remove the

Statistical Record Fhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aacility Messages

following messages are not controlled by the MSG or FLAG PARM and will appearonly on the console.WER500I

STATISTICS DATA SET NOW OVER xx PERCENT FULLEXPLANATION: xx percent of space currently allocated on the SyncSortStatistics data set has been used.

ASYNCSORT STATISTICS DATA SET NOW FULL - NO RECORD

: The SyncSort Statistics data set did not have enough spacefor the SYNCSMF record.

SYNCSORT Messages

APROC SYNCSORT UNSUPPORTED FUNCTION. RETRY,NORETRY

EFFECT

: SyncSort's high performance technique could not be usedduring this invocation by PROC SYNCSORT - An Accelerator for SAS Sort-ing.This may be due to a small region size or the generation of an unsup-ported SyncSort statement syntax. If the RETRY option of PROCSYNCSORT is in effect, SyncSort MVS will be reinvoked using a less effi-cienhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at E15-E35 interface. If the RETRY option is not in effect, the PROCSYNCSORT execution will be terminated.WER744ACONFLICT BETWEEN SYNCSORT AND PROC SYNCSORT MAIN-TENANCE LEVELS, VERIFY LIBRARIES

: Maintenance has been applied to either PROC SYNCSORTor SyncSort MVS, but not to both when maintenance to both is required.ACTION: Check the libraries containing PROC SYNCSORT and SyncSortMVS and apply the required level of maintenance to each.WER775ASAS I/O ERROR OCCURRED. CHECK SAS MESSAGE LOG DATA-SET

: An I/O error occurred when a SAS routine attempted toaccess or update a SAS data set. A message indicating the actual nature ofthe problem should appear on the SAS message LOG data set.WER776ABLDL FAILURE FOR DDNAME SASLIB.RAISE REGION OR

SASLIB ACCESS

: When attempting to perform a BLDL for the library iden-tified by the SASLIB DD statement, an error occurred. The error ihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1as due ei-ther to insufficient virtual storage or a permanent I/O error on the library.

15. Messages15.49

WER777AERROR LOADING PROC SYNCSORT MODULE.CHECK PROC

INSTALL

: The PROC SYNCSORT module (SYNCRI02) could not befound in any of the libraries on the normal MVS search chain or an erroroccurred while loading the module.WER778AUNEQUAL MAINTENANCE APPLIED TO PROC SYNCSORT AND

LIBRARIES.DATA=hexdata

: The maintenance level of the PROC SYNCSORT productis in conflict with the maintenance level of the SyncSort MVS product dueto the incomplete application of one or more maintenance levels. Thehexadecimal data, if printed, indicates which maintenance fixes were in-completely applied.WER779I

PERFORMANCE OF THIS SORT COULD BE SIGNIFICANTLYIMPROVED THROUGH THE USE OF THE PROC SYNCSORTPRODUCT

:PROC SYNCSORT - An Acceleratorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a for SAS Sorting is ahigh performance replacement for the SAS-provided procedure PROC SORT.When SyncSort is invoked with the PROC SYNCSORT product instead ofthrough the interface supplied by SAS, significant performance improve-ments result. For more information, call your Syncsort Representative.

(KEY) Messages

following are the messages directly related to the use of a SyncSort MVS passwordand the KEY installation parameter.

ASYNCSORT NOT AUTHORIZED FOR CPU SERIAL NUMBER nnnnn

: The password(s) provided in the KEY installation param-eter are not valid for use on the specified CPU (nnnnn).Both the serialnumber and the machine model number must be valid.

: Execute the SYNCLIST report program on the system where thismessage is occurring, and ensure that the SYNCMAC KEY parameter hasbeen correctly specified.If the KEY is correct, contact your Syncsort repre-shttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aentative, with the SYNCLIST output available for reference.WER901I

**WARNING** SYNCSORT PRODUCT WILL EXPIRE IN nn DAYSEXPLANATION: The password(s) provided in the KEY installation param-eter are only valid for the next nn days. After that time, WER902A will beissued, and SyncSort will not execute.

: Contact the systems programmer in charge of SyncSort mainte-nance, or contact your Syncsort representative.

.50 Programmer'sGuide

WER902ASYNCSORT PRODUCT HAS EXPIRED

: The password(s) provided in the KEY installation param-eter are no longer valid because the password expiration date has passed.SyncSort will no longer execute.

: Contact the systems programmer in charge of SyncSort mainte-nance, or contact your Syncsort representative.

Abends

with WER999A UNSUCCESSFUL SORT

A indicates that an error condition occhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aurred, preventing the successful com-pletion of the sort. This message does not necessarily mean that SyncSort was responsiblefor the error. If, for example, the error is in the COBOL Input or Output Procedure of anthe error, printing this SyncSort message.

documentation accompanying WER999A varies with the error involved. It may con-sist of a standard system dump (SYSUDUMP or SYSABEND) and/or aSyncSort-generated SNAP dump. The SyncSort SNAP is formatted very much like aSYSUDUMP. In debugging the SNAP, care must be taken to avoid reliance on the PSWAT ENTRY TO SNAP and the general registers. (A SNAP dump produced through theSyncSort DEBUG PARM or with a W-abend (i.e., WER999A UNSUCCESSFUL SORTxxxW) is only useful to a sort analyst at SyncSort MVS Product Services. See &quot;What toDo Before Calling SyncSort MVS Product Services&quot;.)

Internal Abend

W-type abend code indicates that program termihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1anation was forced by an error conditioninternally detected by SyncSort; the problem cannot be resolved by the user. See &quot;Whatto Do Before Calling SyncSort MVS Product Services&quot;, below.

-Issued Abend

any of the following abend codes appear in WER999A, it may indicate a SyncSort error(in which case, see &quot;What to Do Before Calling MVS Product Services&quot;). These are the onlyU-type abend codes that SyncSort issues; any U-type abend code which is not on this listindicates an error in a user-written exit routine or invoking program. Note that WER999Agives the abend code in hexadecimal.

Abend 4093

abend 4093 (RC=1C) is related to LOCALE processing.This abend is issued fromthe LE/370 environment when the REGION is not large enough.Increase the REGIONby 1 megabyte and resubmit the application.

15. Messages15.51

User-Type Abend Codes Issued by SyncSort://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a

*69101999**1024***1025102610271028103010311032105010511052105310541060106110701071107210731074107510761077107810791086108710881102

*45653E7**400***40140240340440640740841A41B41C41D41E42442542E42F43043143243343443543643743E43F44044E

F45045345445645745845B45C45D45E45F46046146246346446546646746846946B4A44A54A64A74A84A94AA4AB4AE800801802

*The RC-16=ABE option is specified and there has been critical error.**The IOERR=ABE option is specified and there has been an I/O error.

***This is most commonly caused by the release of SyncSort's SVC not matching the release of

SyncSort module.

.52 Programmer'sGuide

What to Do Before Calling SyncSorhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at MVS Product Services

pertinent information (listings, dumps, etc.)should be available for easy referencewhen calling SyncSort MVS Product Services. For error conditions producing theWER999A message, the system dump and/or SyncSort SNAP dump will prove helpful toa SyncSort analyst.For other conditions cited with an &quot;A&quot; class message (e.g., WER039AINSUFFICIENT VIRTUAL STORAGE), additional diagnostic information may be re-quired - a diagnostic SNAP dump can be produced by passing the DEBUG PARM in the$ORTPARM DD statement or (for a JCL sort) in the // EXEC statement. When usingDEBUG, supply a SPYSET or SYSUDUMP DD statement to define an appropriateSYSOUT data set for the dump.

the United States and Canada, call SyncSort MVS Product Services directly at (201)930-8260. The address is:

Incorporated

MVS Product Services

Tice Boulevard

Lake, New Jerhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1asey 07675

: (201) 930-8284

-mail: mvs_tech@http://www.wendangwang.com

, call your SyncSort representative.

15. Messages15.53

15.54 Programmer'sGuide

Index

$

$ORTPARM Statement4.1, 4.11-4.14, 5.1, 6.2,7.10, 7.30, 11.5

$ORTPARM, for Year 20004.13$ORTPARM, with CENTWIN4.13

Format2.19, 2.33, 2.109ACS 2.118,5.15

Control Statement2.13-2.14, 6.9, 6.10,7.57

6.13

Operator2.21

Control Characters2.70-2.71AQ Format2.13, 2.19, 2.33, 2.109ASL Format2.19, 2.33, 2.109Assembler Programs1.1

SyncSort from6.1-6.19AST Format2.19, 2.33, 2.109ATTACH Macro6.3, 7.9, 7.29

Messages15.50-15.51Averages, Example3.45AVG 2.64

Messages

BMSG Option

Option5.3, 12.4

Option5.2, 5.33, 6.7, 6.10, 11.2, 11.4,11.5, 12.8

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arBatchPipes/MVS2.56, 4.5, 4.7, 4.8BI Format2.19, 2.33, 2.109

Zeros, Insertion of2.75-2.77, 3.18-3.20Bit Level Comparison2.20

Level Logic2.20-2.21, 2.26-2.28

Option (MAXSORT)5.1, 9.10BLKSIZE Parameter4.4, 5.5, 5.24, 5.27-5.28Block Size5.27-5.28BMSG Option5.3, 5.7BSAM 4.5,4.8

Parameter4.4

E157.19-7.27C E357.43-7.51

Exits7.19-7.27, 7.43-7.51C Programs1.1

Window2.36-2.40, 2.85-2.86,2.111-2.116

I.1

CENTWIN Option2.36-2.40, 2.111-2.116, 5.3,5.8-5.9

Processing, with OUTREC2.98CENTWIN, with $ORTPARM4.13CH Format2.19, 2.33, 2.109CHANGE 2.92

Separation12.15

-Restart 4.14,12.10-12.14Automatic 12.12-12.13Deferred 12.13-12.14

/CHKPT Parameter (MERGE)2.40CKPT/CHKPT Parameter (SORT)2.117CLO Format2.19, 2.33, 2.109CMP Option5.3, 5.10, 12.3CMP=CLC2.36, 5.3, 12.3CMP=CPD2.36, 5http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.3, 12.3

Option5.3, 5.10, 7.10, 7.31COBEXIT=COB1 5.3COBEXIT=COB2 5.3COBOL 35

Exit in OS/VS COBOL7.31Writing Exit in VS COBOL II orCOBOL/370 7.31

E155.15, 7.10-7.19DATA DIVISION7.13

DIVISION7.13EXIT-STATUS Codes7.14

Length Records7.11, 7.15-7.16IDENTIFICATION DIVISION7.13LINKAGE SECTION7.10-7.13PROCEDURE DIVISION7.13RETURN-CODE Codes7.14

Length Records7.12-7.13, 7.17-7.19WORKING-STORAGE SECTION7.13Writing Exit in OS/VS COBOL7.10Writing Exit in VS COBOL II orCOBOL/370 7.10

E355.15, 7.30-7.42DATA DIVISION7.34

DIVISION7.34EXIT-STATUS Codes7.35

Length Records7.31-7.33, 7.37-7.39IDENTIFICATION DIVISION7.34LINKAGE SECTION7.31-7.34PROCEDURE DIVISION7.35RETURN CODE Codes7.35-7.36

Length Records7.33-7.34, 7.40-7.42

.2 Programmer'sGuide

STORAGE SECTION7.34COBOL Exits7.5,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a 7.10-7.19, 7.30-7.42See also COBEXIT OptionCOBOL/370 7.10,7.31OS/VS COBOL7.10, 7.31VS COBOL II7.10, 7.31COBOL Programs1.1, 6.1, 12.2COBOL, and Year 20004.13COBOL/370

COBOL E35See COBOL Exits

Parameter (ALTSEQ)2.13Coding Conventions4.3-4.4

Sequence2.13-2.14, 2.33, 7.57Combining Records in a File3.11-3.13COMMAREA Option5.3, 5.11, 7.4Communication Area5.11

Area for Exits7.4

Fields2.18-2.29, 2.111, 3.3-3.11See also CMP Option

Level Criteria2.20-2.21Constants 2.19

to Constant Comparison2.24

and ZD Field Comparison2.36, 2.111,5.10

for Specifying Fields2.35Concatenating Input Data Sets4.6

Parameter (INCLUDE/OMIT)2.18-2.29Control Statement Syntax2.8-2.11Control Statements2.1-2.124

also $ORTPARM StatementSee also Job Control LanguageSee also SYSIN Statement

.13-2.14, 6.9, 6.10, 7.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a57Coding in Invoked Programs6.2Comments in2.10

of2.10-2.11DEBUG 6.9Defaults 2.3-2.5END2.15, 6.3, 11.7for MAXSORT9.10for Tape Sort11.7

/OMIT2.16-2.29, 3.3-3.6, 5.17,5.29, 6.9, 12.2

.30-2.31, 3.6-3.11, 6.9, 12.2, 12.3Labels in2.11

MERGE2.30, 2.32-2.42, 5.15, 5.17, 5.29, 6.3,6.8, 7.56, 7.57

.43-2.46, 5.15, 6.3, 6.5, 6.9, 11.7Notational Conventions2.11OMIT 2.47

.30, 2.48-2.73, 3.26-3.53, 6.2, 6.10,12.2

.30, 2.74-2.102, 3.14, 6.9, 12.2,12.3

Considerations12.2-12.3Processing Sequence2.6-2.7RECORD2.103-2.107, 6.3, 11.7Requirements for Disk Sort2.5Requirements for MAXSORT2.5Requirements for Tape Sort2.5Rules for Specifying2.8-2.11SORT 2.30,2.107

Field Formats in2.9Specifying Field Lengths in2.9Specifying Field Positions in2.9Specifying Parameters in2.8-2.9

.30, 2.121-2.124, 3.11, 5.16, 5.17, 6.9,7.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a27, 12.2

of Functions2.1

of Parameters and Defaults2.3-2.5Summary of the Chapter1.6

in Invoked Applications6.3-6.4CONVERT Parameter (OUTFIL)2.55CONVERT Parameter (OUTREC)2.95Converting Data2.80-2.81, 2.86, 3.20-3.27Format 2.80-2.81

Variable Length Records2.55, 2.77,2.95, 3.26-3.27

Year Data2.85-2.86Copy

Input Data Sets for4.5Flow of8.1-8.6Copying 1.2

of1.2

Option5.3, 5.12, 12.4-12.6COUNT 2.65COUNT15 2.66

Option5.3, 5.7, 5.13, 12.4CRCX Option5.33, 6.7, 6.10CSF Format2.19

Format2.19, 2.33, 2.109CST Format2.19, 2.33, 2.109

Format2.19, 2.33, 2.35, 2.109, 2.110Cultural Environment1.5, 2.32, 2.107, 5.21

Data Set4.4

Set Placement12.14-12.15Data Utility3.1-3.53

Records3.11-3.13Examples, Index to3.2Features of1.3, 3.1

Record Selehttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1action3.3-3.11Input Records, Selection of RelevantFields 3.6-3.11

Files, Multiple3.51-3.53Output Records

Data3.23-3.24

Data to HexadecimalFormat 3.22-3.23

Data to ReadableForm 3.20-3.21

Data3.23-3.24Editing of3.13-3.27

Data Fields3.25-3.27Inserting Binary Zeros2.75-2.77,3.18-3.20

Blanks3.16-3.18

Field Positions3.14-3.18Output Reports

Data Records3.47-3.51Headers and Trailers for3.31-3.39Sectioning of3.29-3.31

and Subtotaling Data3.39-3.44Sample Applications, Summarized3.2Summary of the Chapter1.6DATE (&amp;DATE)2.58, 2.62DCB Information2.103

Parameter4.4, 5.5, 5.24, 5.27

Statements4.4-4.16, 9.4-9.10, 10.2-10.3,11.3-11.5

also Exit Programs, Link-editing

$ORTPARM Statement4.11-4.14, 6.2, 11.5Coding Conventions4.3-4.4JOBLIB Statemenhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1at4.4ParametersAMP 4.4

I.3

BLKSIZE 4.4BUFND 4.4BUFNI 4.4BUFOFF 4.4BUFSP 4.4DCB 4.4DISP 4.4

/DSN 4.4LABEL 4.4LRECL 4.4OPTCD 4.4RECFM 4.4SPACE 4.4UNIT 4.4

/VOL 4.4

Statement9.6-9.7SORTCKPT Statement4.14, 12.2SORTIN Statement4.5-4.7, 6.2SORTINn Statement4.7SORTINnn Statement6.2SORTLIB Statement6.2, 11.4SORTMODS Statement4.15SORTOFx Statement4.8, 6.2SORTOFxx Statement4.8, 6.2

Statement9.7-9.9, 9.10SORTOUT Statement4.8, 6.2SORTPARn Statement10.5-10.7SORTWKnn Statement4.9-4.11, 6.2,11.4-11.5

4.8

Statement4.4

for Invoked Sort/Merge6.1-6.2SYSIN Statement4.11SYSLIN Statement4.15SYSLMOD Statement4.15SYSOUT Statement4.4, 6.2SYSPRINT Statement4.15SYSUT1 Statement4.16ddname4.1, 9.5, 10.3, 11.3DEBUG Control Statement6.9DEBUG Option5.3, 5.13Defining Output Data SetsSee SORTOUT Files

SORTOUT StatementDefining Whttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aork Areas

SORTWKnn StatementDevice Separation12.15

.4 Programmer'sGuide

Option5.3, 5.13, 6.7, 6.10Disk Sort4.1, 12.8

Statements2.1-2.124DD Statements for4.1-4.16Device Types4.9

Statement for4.3PARM Options11.1

Options5.1-5.33

Considerations12.1DISP Parameter4.4, 5.27DSN Parameter

DSNAME ParameterDSNAME Parameter4.4Duplicate Records3.11-3.13

Option4.1, 5.3, 5.14-5.15

Parameter (SORT)2.117-2.118DYNATAPE Option (MAXSORT)4.1, 5.1, 9.11,9.15-9.17

2.45

2.45,7.5

.10, 5.17, 7.7-7.8, 9.14

.45, 5.17, 7.7, 7.8-7.10, 7.58, 9.14, 11.8,11.10, 13.5

also COBOL E15E15 Option5.3, 5.15, 7.10E15=COB 5.4

.10, 7.51, 9.14E17 7.52

7.52-7.55E20 2.45

2.45,7.5

.7, 7.27-7.28, 9.14E27 7.52E30 2.45

2.45,7.5

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arE322.41, 6.2, 7.5, 11.8

.2, 7.7, 7.28-7.30, 7.58, 9.14, 11.8, 11.10See also COBOL E35E35 Option5.3, 5.15E35=COB 5.4E37 7.52

7.52-7.55

7.52,7.55-7.56

E612.45, 7.56-7.58, 9.14EDIT 2.65

Patterns2.86-2.88, 2.91, 3.24EDIT Subparameter2.86

Data2.82-2.94, 3.13-3.27Editing Masks2.65, 2.88-2.91

Option5.3, 5.4, 5.7, 5.15, 12.4END Control Statement2.15, 11.7ENDREC Parameter (OUTFIL)2.53

-keyed Records2.41, 2.118, 2.121, 5.16EQUALS Option5.4, 5.16, 12.3EQUALS/NOEQUALS Parameter(MERGE) 2.41

/NOEQUALS Parameter (SORT)2.118Esoteric Names10.7

Statement4.3, 9.4, 10.2, 11.2for Disk Sort4.3

MAXSORT4.3, 9.4for PARASORT10.2

Tape Sort4.3, 11.2-11.3Exit Conventions

MVS/XA Exit ConventionsExit Programs2.43-2.46, 7.1-7.60

on Insufficient Storage7.51Adding Records7.28-7.30

Sorthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a Input File7.8-7.10Changing Records7.7-7.8, 7.27-7.30Checking Labels7.52-7.55Closing Exit Data Sets7.52Communication Area7.4

Input Records7.5-7.10Creating Sort Input File7.8-7.10Definition of7.1

Records7.7-7.8, 7.27-7.30End-of-File Routines7.52-7.55for Invoked Merge7.5

in MODS Control Statement7.3Link-editing 7.3

-editing at Execution Time

Statements Required for4.14-4.16Loading into Main Storage7.3MAXSORT 9.14

Collating Sequence7.56-7.58MVS/XA Exit Conventions7.3Phases 7.1-7.2

for Other Exit Programs7.5Processing Read Errors7.52-7.55

Write Errors7.52-7.55Program Labels7.1

Conventions7.4

Sort Input File7.8-7.10

Records7.7-7.8, 7.27-7.28Summary of Tasks Performed7.2Summary of the Chapter1.7VSAM Processing7.52with Disk Sort2.45

MAXSORT2.45, 9.14with Phttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aARASORT2.45

Tape Sort2.45, 11.8, 11.10Exit Programs, Link-editing4.16

-Name Parameter (MODS)2.43-2.45EXTCOUNT 5.4,5.16EXTCOUNT Option5.3

Format2.19, 2.33, 2.109Field ComparisonSee CMP Option

Format Codes2.33-2.35, 2.108-2.110AC2.19, 2.33, 2.109

.13, 2.19, 2.33, 2.109ASL2.19, 2.33, 2.109AST2.19, 2.33, 2.109BI2.19, 2.33, 2.109CH2.19, 2.33, 2.109CLO2.19, 2.33, 2.109CSF 2.19

.19, 2.33, 2.109CST2.19, 2.33, 2.109

.19, 2.33, 2.35, 2.109, 2.110FI2.19, 2.33, 2.109FL 2.33,2.109FS 2.19

of Valid Formats2.33-2.35, 2.109-2.110LS 2.19

.19, 2.33, 2.109

.19, 2.35, 2.109, 2.110P2ID 2.85P2IP 2.85

.19, 2.33, 2.109

.19, 2.34, 2.39, 2.109, 2.115TS2.19, 2.33, 2.109

I.5

Y2B2.19, 2.34, 2.36, 2.85, 2.110, 2.112Y2C2.19, 2.34, 2.37, 2.85, 2.110, 2.112Y2D2.19, 2.34, 2.37, 2.85, 2.110, 2.113Y2P2.19, 2.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a34, 2.38, 2.85, 2.110, 2.113Y2S2.19, 2.35, 2.39, 2.85, 2.110, 2.114Y2Z2.19, 2.35, 2.37, 2.85, 2.110, 2.112ZD2.19, 2.35, 2.109, 2.110Fields 2.74-2.102

.16, 2.20-2.21, 2.108Bit Level Comparison2.20

of2.18-2.29, 2.111, 3.3-3.11Constants 2.19

.33-2.35, 2.53, 2.83, 2.108-2.110Insertion of Binary Zeros3.18-3.20Insertion of Blanks3.16-3.18Length 2.108

2.81,2.108Reordering 3.14-3.18

for Specifying2.35, 2.111Selection of3.6-3.11Specifying Format2.9Specifying Length2.9, 3.6Specifying Position2.9, 3.6Substring Comparison2.25FIELDS Parameter (INREC)2.31

Parameter (MERGE)2.32-2.40FIELDS Parameter (OUTREC)2.75-2.94FIELDS Parameter (SORT)2.108-2.116FIELDS Parameter (SUM)2.121-2.122FIELDS Subparameters2.78Operator 2.80

=COPY2.40, 2.41, 2.116FIELDS=NONE 2.121File Size

FILSZ Option

Parameter (MERGE)2.41

Parameterhttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a (OUTFIL)2.50-2.51, 3.51-3.53FILSZ Option5.4, 5.17

Parameter (SORT)2.119

Length Records2.9, 2.35, 2.77, 2.95, 2.103,7.11, 7.15-7.16

Length4.5FL Format2.33, 2.109

Option5.4, 5.18, 6.10Flow of the Sort8.1-8.6

Parameter (OUTFIL)2.51-2.52

.6 Programmer'sGuide

.17, 2.32, 2.33, 2.53, 2.107, 2.108,2.120, 2.121, 2.124SORT 2.120

Programs1.1, 6.1FS Format2.19

2.44,6.3

, OUTFIL2.51, 2.52, 2.55

Option4.5, 5.4, 5.18HBSO Option4.9, 5.4, 5.18

/ HEADER2 Parameter(OUTFIL) 2.56-2.60,3.31HFS4.5, 4.7, 4.8Hiperbatch 5.18

Processing5.18

.105-2.106, 5.20, 7.8, 13.1-13.13Control Parameters13.2-13.4Executing through E1513.5-13.7Job Control Language13.4Messages 13.10-13.13

Samples13.8-13.9Summary of the Chapter1.7

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a/OMIT Control Statement2.16-2.29,3.3-3.6, 5.17, 5.29, 6.9, 12.2INCLUDE/OMIT Parameter(OUTFIL) 2.52-2.53

Option5.4, 5.19, 12.6

Sort2.40, 2.117, 2.123, 5.19, 8.1, 12.6INCORE=OFF 5.4INCORE=ON 5.4Input Data Sets

of4.6Input Records

of3.3-3.11

Control Statement2.30-2.31, 3.6-3.11,6.9, 12.2, 12.3

Installation Guide1.7Installation Options

Rules5.2

Storage4.9-4.10, 11.4

SyncSort from a Program6.1-6.19Assembler Program6.19Assembler Programs6.2DD Statements6.1

Instructions for Invoking SyncSort froman Assembler ProgramATTACH 6.2LINK 6.2LOAD 6.2XCTL 6.2MAXSORT 9.14

Considerations6.1

on Control Statements6.3-6.4Tape Sort11.10-11.13

Option5.3, 5.5, 5.7, 5.19, 12.4IOERR Option5.4, 5.19, 6.10IOERR=ABE 5.5

also Job Cohttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1antrol Languagefor PARASORT10.2

Control Language4.1, 4.16Control Statement Examples

without Exit Routines4.25-4.27Merge without Exit Routines4.23-4.24Multiple Output Files4.32Sort with Exit Routine to beLink-edited 4.29-4.32Sort with Link-edited ExitRoutine 4.27-4.29

without Exit Routines4.22DD Statement4.1Elements of4.1

Statement4.1, 5.1, 6.1for HISTOGRM13.4for MAXSORT9.4, 9.14for Tape Sort11.8-11.10Initiating SyncSort4.11, 6.1JOB Statement4.1

without Exit Routines4.17

of the Chapter1.6

Statement4.4

Messages15.50-15.51

Option5.4, 5.20, 13.1L7 Option5.4, 5.20, 13.1LABEL Parameter4.4, 5.28

Environment for MVS1.5, 5.21LENGTH 2.65

Parameter (RECORD)2.103-2.105LENGTH Subparameter2.87

Parameter (OUTFIL)2.68-2.71LINK Macro6.3, 7.9, 7.29

Option5.4, 5.21, 6.7,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a 6.10LOAD Macro6.3LOCALE

with INCLUDE/OMIT2.16LOCALE Option5.5, 5.21, 7.57

.60, 2.66, 2.69, 2.104, 2.105

Parameter4.4, 5.5, 5.24, 5.27-5.28, 5.31LS Format2.19

Instructions (Assembler)6.2-6.3ATTACH Macro6.2LINK Macro6.2LOAD Macro6.2XCTL Macro6.2Masks 2.65MAX 2.64

, Example3.45

.48, 4.1, 4.7, 4.10, 9.1-9.22, 11.1DD Statements for4.16, 9.4-9.10EXEC Statement for4.3, 9.4Exit Programs9.14File Size4.7

from a Program9.14

/Control Stream Examples9.18-9.22

I.7

Operator Interface9.15-9.17

Options4.3, 5.1, 9.10-9.14BKPTDSN 5.1,9.10

.1, 9.11, 9.15-9.17MAXSORT 9.11

5.1,9.11MINWKSP 5.1,9.12

5.1,9.11RESTART 5.1,9.12SORTSIZE 5.1,9.13SORTTIME 5.1,9.13TAPENAME 5.1,9.13

Considerations9.22, 12.1PGM Names4.3Starting 9.14-9.15

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arStarting through JCL9.4, 9.14

of Control Statements for2.5Summary of the Chapter1.7Tuning 9.22

Option (MAXSORT)9.11

Option (MAXSORT)5.1, 9.11Merge

Input Data Sets4.7

Input Records for InvokedMerge 7.5Flow of8.1-8.6

Control Statement2.30, 2.32-2.42, 5.15,5.17, 5.29, 6.3, 6.8, 7.5, 7.56, 7.57Merging 1.2

of1.2

Data Set5.24-5.25

.4, 5.7, 5.18, 5.23-5.24, 15.1-15.53See also FLAG Option

Messages15.50-15.51KEY Messages15.50-15.51

SYNCSORT Messages15.49-15.50Statistical Record Facility Messages15.49Summary of the Chapter1.7MIN 2.64

, Example3.45

Option (MAXSORT)5.1, 9.12Mm Subparameter2.88

Control Statement2.43-2.46, 5.15, 6.3,6.5, 6.9, 7.3, 7.5, 7.9, 7.10, 7.29, 7.30, 7.31, 11.7MSG Option5.4, 5.23-5.24, 6.10MSGDD Option5.4, 5.24, 7http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.10, 7.31Multiple Lines, Record2.55

.8 Programmer'sGuide

Output2.51, 2.52, 3.51-3.53Multiple Output Files2.49MVS/XA Exit Conventions7.3

Language1.5, 2.16, 2.32, 2.107, 5.21with INCLUDE/OMIT2.16NOCOMMAREA Option5.3, 5.11

Parameter (OUTFIL)2.71

Option (MAXSORT)5.1, 9.11NOEQUALS Option5.4, 5.16NOIOERR Option5.4, 5.19NOLIST Option5.4, 5.21NORC16 Option5.5, 5.25NORESET Option5.5, 5.27NORLSOUT Option5.5, 5.27Notational Conventions2.11NZDPRINT 5.7

Option5.32

Format2.19, 2.33, 2.109

Control Statement2.47, 3.6Operator 2.80

Interface9.15-9.17OPTCD Parameter4.4OR Operator2.21OS/VS COBOL

COBOL E15See COBOL E35

Option5.2, 5.33, 6.7, 6.10, 11.2, 11.4, 11.5,12.8

2.110

Format2.19, 2.35, 2.109

Control Statement2.30, 2.48-2.73,3.26-3.53, 6.2, 6.10, 1http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a2.2

Group2.51, 2.52, 2.55Output Data Sets4.8, 4.9See also SORTOUT Files

also SORTOUT Statement

Files, Multiple2.49, 3.51-3.53, 4.32-4.33Output Lines, Multiple2.55, 2.57, 3.29Output Records

Converting Data3.20-3.27Editing Data3.23-3.27

.54-2.55, 2.74-2.102, 3.13-3.27Output Records, Distributing2.55Output Reports2.48-2.73, 3.29-3.53Averaging Data3.45

Record Number2.53Headers 2.56-2.71,3.31-3.39Obtaining maximums3.45Obtaining minimums3.45Pages, Logical2.68-2.71Records Included2.53Saving Records2.54

2.67-2.68,3.29-3.31Starting Record Number2.53Subtotaling Data3.39-3.44Totaling Data3.39-3.44

.60-2.67, 2.68-2.71, 3.31-3.51Output Space

Secondary Allocation

Control Statement2.30, 2.74-2.102,3.14, 6.9, 12.2, 12.3

Parameter (OUTFIL)2.54-2.55

(&amp;PAGE)2.59, 2.63

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1ages, Defining Logical2.68-2.71Parameter List

-bit 6.4-6.13,7.3

Parameters6.8-6.1031-bit 6.13-6.19,7.3Parameters

of the Chapter1.6Parameters (Control Statements)CKPT/CHKPT 2.40,2.117CODE 2.13

2.18-2.29

.55, 2.95, 3.26-3.27DYNALLOC 2.117-2.118ENDREC 2.53

/NOEQUALS 2.41,2.118Exit-Name 2.43-2.45

.31-2.40, 2.75-2.94, 2.108-2.116,2.121-2.122

.41, 2.50-2.51, 3.51-3.53

2.119

2.51-2.52HEADER 12.3

/HEADER2 2.56-2.60,3.31INCLUDE/OMIT 2.52-2.53LENGTH 2.103-2.105LINES 2.68-2.71NODETAIL 2.71

2.54-2.55,12.3SAVE 2.54

.67-2.68, 3.29, 12.3SIZE 2.105,2.119

.41, 2.119, 12.3SPLIT 2.55-2.56STARTREC 2.53

.42, 2.119, 12.3TRAILER 12.3

/TRAILER22.60-2.67, 3.31, 3.47TYPE 2.103XSUM 2.122

(DD Statements)AMP 4.4

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aZE4.4, 5.5, 5.24, 5.27-5.28BUFND 4.4BUFNI 4.4BUFOFF 4.4BUFSP 4.4

.4, 5.5, 5.24, 5.27DISP 4.4,5.27

/DSN 4.4LABEL 4.4,5.28

.4, 5.5, 5.24, 5.27-5.28, 5.31OPTCD 4.4

.4, 5.5, 5.24, 5.27-5.28SPACE4.4, 5.5, 5.25UNIT 4.4

/VOL 4.4

.1, 4.7, 10.1-10.9

Statements for4.16, 10.2-10.3EXEC Statement for10.2JCL for10.2

/Control Stream Examples10.9PARM Options4.3PGM Names4.3

Statement for10.3Summary of the Chapter1.7PARASORT Sort

I.9

DD Statements for4.16PARASORTt

Options5.2PARM Options5.1-5.33

also $ORTPARM StatementBALANCE5.3, 5.7, 12.4

.2, 5.33, 6.7, 6.10, 11.3, 11.4, 11.5,12.8

5.1BMSG 5.3,5.7

.36-2.40, 2.111-2.116, 5.3,5.8-5.9

5.10,12.3CMP=CLC 2.36CMP=CPD 2.36

.10, 7.10, 7.31COMMAREA 5.11,7.4CORE 5.12,12.4-12.6CPU5.3, 5.7,http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a 5.13, 12.4CRCX5.33, 6.7, 6.10DEBUG 5.13

.13, 6.7, 6.10

4.1,5.14-5.15DYNATAPE 4.1,5.1E15 5.15,7.10E35 5.15

.3, 5.4, 5.7, 5.15, 12.4EQUALS5.4, 5.16, 12.3EXTCOUNT 5.4,5.16FILSZ 5.4,5.17

.4, 5.18, 6.10for Disk Sort5.1-5.33

MAXSORT5.1, 9.10-9.14for PARASORT5.2for Tape Sort5.2Format of5.1

.5, 5.4, 5.18HBSO4.9, 5.4, 5.18INCOR 5.4

.4, 5.19, 12.6IO5.3, 5.5, 5.7, 5.19, 12.4IOERR5.4, 5.19, 6.10L65.4, 5.20, 13.1L75.4, 5.20, 13.1

.4, 5.21, 6.7, 6.10LOCALE5.5, 5.21, 7.57MAXWKSP 5.1I.10 Programmer'sGuide

5.1

.4, 5.23-5.24, 6.10MSGDD5.4, 5.24, 7.10, 7.31NOCOMMAREA 5.11NODYNATAPE 5.1NOEQUALS 5.4,5.16NOIOERR 5.4,5.19NOLIST 5.4,5.21NORC16 5.5,5.25NORESET 5.5,5.27NORLSOUT 5.5,5.27NZDPRINT 5.7,5.32

.2, 5.33, 6.7, 6.10, 11.3, 11.4, 11.5,12.8

.33, 6.7, 6.10

.2, 5.33, 6.7, 6.10, 11.3, 11.4, 11.http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a5,12.8

Rules5.2PRINT121 5.5,5.24RC165.5, 5.25, 6.10

.5, 5.25, 12.6RESERVE 5.5,5.26RESERVEX 5.5,5.26RESET 5.5,5.27RESTART 5.1RLSOUT 5.5,5.27SDB 5.5,5.27-5.28

.5, 5.28, 12.6SIZE 5.12

.5, 5.29, 7.52, 12.3SORTSIZE 5.1SORTTIME 5.1

in JCL-initiatedApplications 5.1

in Program-initiatedApplications 5.1

.5, 5.29, 12.3Summarized 5.2-5.7TAPENAME 5.1UNINTDS 5.6,5.30VLTEST5.5, 5.30, 12.3VLTESTI 5.6,5.31VSAMEMT 5.6,5.32ZDPRINT 5.7,5.32

Format2.19, 2.33, 2.36, 2.109, 2.111, 5.10PD0 Format2.19, 2.34, 2.39, 2.109, 2.115PDID Format2.85

PDIP Format2.85

Option5.33, 6.7, 6.10

Considerations12.1-12.15Control of System Resource Usage12.3Control Statements12.2-12.3

- vs. Program-Invoked Sort12.2Memory Management12.3-12.6PARMS Options12.3

of the Chapter1.7

://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aases of Copying, Merging, Sorting8.1-8.6PipeSort1.6, 2.50, 3.51, 14.2PL/1 Programs1.1, 6.1

Option5.2, 5.33, 6.7, 6.10, 11.2, 11.4,11.5, 12.8

Rules5.2

Option5.5, 5.24

SYNCSORT - An Accelerator for SAS&#174;Sorting 1.6,14.2

SYNCSORT Messages15.49-15.50Program Exits

Exit Programs

Option5.5, 5.25, 6.10RC16=ABE 5.5

.9, 2.95, 2.104

Parameter4.4, 5.5, 5.24, 5.27-5.28RECORD Control Statement2.103-2.107, 6.3,11.7

Counts3.47-3.51Record Format2.103-2.107Record Length2.103-2.107

for Fixed Length Records4.5Maximum for Variable Length Records4.5Record Selection2.16-2.29, 2.41-2.42, 2.52-2.53,2.119, 3.3-3.11, 5.29

Bit Level Logic2.26-2.28Records, Distributing Output2.55Reference Guide1.8

Records2.30-2.31, 2.48, 2.54-2.55,2.74-2.102, 3.14-3.18

Subpahttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1arameter2.92Column Alignment2.57

Conversion and Editing2.82-2.98,3.20-3.26

Binary Zeros2.76, 3.18Inserting Blanks or Spaces2.76

Hexadecimal Characters2.76Inserting Literal Characters2.76OUTREC Parameter2.54-2.55Record on Multiple Lines2.55Replace 2.92

and Replace2.92

Length Records2.77Register Conventions7.4Registers

Register Conventions

Option5.5, 5.25, 12.6Replace 2.92

Writing2.50, 2.56-2.73, 3.29-3.53Repositioning Record Fields3.14-3.18RESERVE Option5.5, 5.26RESERVEX Option5.5, 5.26RESET Option5.5, 5.27

Option (MAXSORT)5.1, 9.12RETRY 2.118,5.14

Codes6.11, 6.16REXX Exits2.44, 7.58-7.60REXX Programs1.1

Option5.5, 5.27

Parameter (OUTFIL)2.54SC 2.118,5.14

.18, 4.19, 4.22, 4.25, 4.30SDB Option5.5, 5.27-5.28Search and Replace2.92

Optihttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aon5.5, 5.28, 12.6Secondary Allocation4.9, 4.10, 5.28

Parameter (OUTFIL)2.67-2.68, 3.29SEQNUM 2.30,2.76SIGNS 2.65

Option5.3, 5.12

Parameter (SORT)2.105, 2.119SKIPREC Option5.5, 5.29, 7.52, 12.3SKIPREC Parameter (MERGE)2.41SKIPREC Parameter (SORT)2.119SNAP Dump5.13Sort

Input Data Sets for4.5

I.11

Flow of8.1-8.6Sort Control

of the Chapter1.7

Control Statement2.30, 2.107-2.120, 5.15,5.17, 5.29, 6.3, 7.52, 7.56, 7.57, 11.7SORT/MERGE 6.2-6.4SORT/MERGE OptionsPrecedence Rules5.2

Statement9.6-9.7SORTCKPT Statement4.1, 4.14SORTIN End-of-File7.9, 7.14

File4.1, 4.5, 5.4, 5.18, 6.8, 6.13, 6.19,7.8, 7.9, 7.11, 7.12, 7.13, 7.14, 7.51SORTIN Processing7.52, 7.53

Statement4.1, 4.5-4.7, 5.28, 6.2, 7.9,10.3

PARASORT10.3Sorting

of1.2Types of1.2Sorting Technique

Sort4.1http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a, 4.9, 11.1, 12.1

.1, 4.7, 4.9, 4.10, 4.16, 9.1-9.22,11.1, 12.1

.1, 4.16, 10.1-10.9Performance Considerations12.1Tape Sort4.1, 4.10, 4.16, 11.1Balanced (BALN)11.4, 11.5Oscillating (OSCL)11.4, 11.5Polyphase (POLY)11.4, 11.5SORTINn Statement4.1, 4.7SORTINnn Statement4.7SORTINnn File5.16, 7.5

Statement4.1, 4.7, 6.2, 7.5SORTLIB Statement6.2, 11.4SORTMODS Library7.3

Statement4.1, 4.15SORTOFx File5.27-5.28

Statement4.1, 4.8, 6.2SORTOFxx File5.6, 5.27, 7.30, 7.35SORTOFxx Statement4.1, 4.8, 6.2SORTOU00 Statement9.7-9.9, 9.10

File4.1, 4.8, 5.4, 5.6, 5.18, 5.27-5.28,7.30, 7.35, 7.52

Files6.2

Space5.6, 5.27

Statement4.1, 4.8, 6.2, 7.29I.12 Programmer'sGuide

VSAM File5.27SORTOUT Write Errors7.55SORTPARn Statement10.5-10.7

Option (MAXSORT)5.1, 9.13SORTTIME Option (MAXSORT)5.1, 9http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1a.13SORTWK

Allocation of5.14SORTWK Requirements11.4SORTWKnn File7.7

Statement4.1, 4.9-4.11, 6.2,11.4-11.5

also DYNALLOC OptionConditions of Use4.10SortWriter2.48, 2.50, 2.56Sample Report1.4SORTXSUM 4.8,5.27

Statement6.2

Parameter4.4, 5.5, 5.25Special Esoteric Names10.7

Parameter (OUTFIL)2.55-2.56Starting SyncSort1.1

of the Chapter1.6

Parameter (OUTFIL)2.53Statistical Record Facility Messages15.49STEPBLIB Statement4.1STEPLIB Statement4.4

Option5.5, 5.29, 12.3

Parameter (MERGE)2.42STOPAFT Parameter (SORT)2.119Storage

4.9

4.9-4.10,11.4SUBAVG 2.65SUBCOUNT 2.66SUBCOUNT15 2.66SUBMAX 2.64SUBMIN 2.64

Comparison2.25SUBTOTAL 2.64

Control Statement2.30, 2.121-2.124, 3.11,5.16, 5.17, 6.9, 7.27, 12.2SyncSort

Utility1.3, 3.1-3.53Deschttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aription of1.1Features of1.1-1.5Initiation of1.1SortWriter 1.4

SyncSort Messages4.4

/COBOL Advantage1.5, 14.1SYSIN Statement4.1, 4.11SYSLIN Statement4.1, 4.15SYSLMOD Statement4.1, 4.15SYSOUT

Message Data Set

Statement4.1, 4.4, 6.2SYSPRINT Statement4.1, 4.15System Abend (0C7)5.10, 5.31SYSUT1 Statement4.1, 4.16

Sort4.1, 4.14, 11.1-11.13, 12.8-12.9Control Statements for11.7Converting to MAXSORT12.2DD Statements for4.16, 11.3-11.5Device Types4.10Devices 11.4

Statement11.2-11.3EXEC Statement for4.3

from a Program11.10-11.13JCL/Control Stream Examples11.8-11.10PARM Options4.3, 11.2

.2, 11.2, 11.4, 11.5, 12.8OSCL5.2, 11.2, 11.4, 11.5, 12.8POLY5.2, 11.2, 11.4, 11.5, 12.8PARMS Options5.2

Considerations12.1PGM Names4.3

4.10,11.8-11.13

through JCL11.8-11.10

of Control Sthttp://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aatements for2.5Summary of Restrictions11.1-11.2

Option (MAXSORT)5.1, 9.13The INCORE PARM is set to OFF.4.10TIME (&amp;TIME)2.59, 2.63TOTAL 2.63

/TRAILER2 Parameter(OUTFIL)2.60-2.67, 3.31, 3.47TS Format2.19, 2.33, 2.109Turnaround SortSee Incore Sort

Parameter (RECORD)2.103

Option4.7, 5.3, 5.6, 5.30UNIT Parameter4.4

-Added Products1.5-1.6, 14.1-14.2PipeSort 1.6,14.2

SYNCSORT - An Accelerator for SAS&#174;Sorting 1.6,14.2

of the Chapter1.7

/COBOL Advantage1.5, 14.1

Length Records2.9, 2.35, 2.77, 2.95,2.103, 3.9-3.11, 7.12-7.13, 7.17-7.19, 7.33-7.34,7.40-7.42

also VLTEST OptionMaximum Length4.5Validity Testing5.30

Option5.3, 5.5, 5.30, 12.3VLTESTI Option5.3, 5.6, 5.31VOL Parameter

VOLUME ParameterVOLUME Parameter4.4VS COBOL II

COBOL E15See COBOL http://www.wendangwang.com/doc/1956270ec6043c02ae4f6c1aE35

.5, 4.8, 5.27, 7.54-7.55VSAM SORTOUT5.6

Option5.6, 5.32

Areas

SORTWKnn StatementWork Space5.6, 5.20, 5.25, 5.27

Macro6.3, 7.9, 7.29XSUM 2.122

Parameter (SUM)2.122

I.13

Y

B Format2.19, 2.34, 2.36, 2.85, 2.110, 2.112Y2C Format2.19, 2.34, 2.37, 2.85, 2.110, 2.112Y2D Format2.19, 2.34, 2.37, 2.85, 2.110, 2.113Y2P Format2.19, 2.34, 2.38, 2.85, 2.110, 2.113Y2S Format2.19, 2.35, 2.39, 2.85, 2.110, 2.114Y2Z Format2.19, 2.35, 2.37, 2.85, 2.110, 2.112Year 2000 Processing2.36-2.40, 2.98-2.116Year 2000, with $ORTPARM4.13

Data, Converting2.85-2.86

Format2.19, 2.35, 2.36, 2.109, 2.110, 2.111,5.10

5.7

Option5.32

.14 Programmer'sGuide

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 https://www.wendangwang.com/

亿万文档资料，等你来发现