本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03

松下AW-HE50 高清摄像机TCP IP网络控制协议

松下AW-HE50 高清摄像机TCP/IP网络控制协议

-HE50

TCP/IP Control Protocol Specifications

1.02

System Networks Co., Ltd.

History

1.00 1.01 1.02

Aug. 25, 2010 Oct. 4, 2010 Oct. 8, 2010

- 5

the first edition of the Specifications. Added a description of Camdata.html.

the #GI command on page 17 and the OAW command on page 38, and made other modifications.

for change

-

. Introduction.......................................................................................................................................4 2. Configuration outline.........................................................................................................................4 3. Camera and pan-tilt head control...........................................................http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03...........................................5 3.1.

-tilt head control...................................................................................................................5

ON/OFF...................................................................................................................8 Installation position.............................................................................................................8 Pan/tilt.................................................................................................................................9 Movement range limit ON/OFF.........................................................................................11 Lens operations................................................................................................................14 Lens information notification ON/OFF..........................................................http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03.....................19 Preset...............................................................................................................................20 Tally...................................................................................................................................21 Zoom position-linked pan/tilt speed adjustment ON/OFF..................................................22 Lens operations................................................................................................................26 Color bar ON/OFF.............................................................................................................32 Scene file setting...............................................................................................................32 Shutter mode setting.........................................................................................................33 Frame mix setting.....http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03........................................................................................................35 Gain setting.......................................................................................................................36 Chroma level setting.........................................................................................................37 AWB setting......................................................................................................................38 Detail setting.....................................................................................................................40

.1.1. 3.1.2. 3.1.3. 3.1.4. 3.1.5. 3.1.6. 3.1.7. 3.1.8. 3.1.9. 3.2. 3.2.1. 3.2.2. 3.2.3. 3.2.4. 3.2.5. 3.2.6. 3.2.7. 3.2.8. 3.2.9.

control.........................................................................................................................23

.2.10. Flesh Tone Mhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ode setting...................................................................................................40 3.2.11. Digital noise reduction (DNR) setting................................................................................41 3.2.12. Pedestal setting................................................................................................................42 3.2.13. DRS setting.......................................................................................................................43 3.2.14. Backlight compensation setting.........................................................................................45 3.2.15. Genlock setting.................................................................................................................46 3.2.16. Output setting....................................................................................................................49 3.2.17. Presethttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 playback range setting...........................................................................................51 3.2.18. Digital zoom ON/OFF setting............................................................................................51 3.2.19. Camera information acquisition.........................................................................................52 3.2.20. OSD menu........................................................................................................................53 4. Camera information update notification...........................................................................................54 4.1. 4.2. 4.3.

for receiving the update notifications......................................................................54 Data format for update notifications.........................................................................................56 Setting change sequencehttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03.........................................................................................................57

.3.1. 4.3.2. 4.3.3. 4.4. 4.4.1. 4.4.2. 4.4.3. 4.4.4. 4.4.5.

the settings from a terminal..............................................................................57 Initialization using OSD menu...........................................................................................59 Scene file selection...........................................................................................................61 Version information notification.........................................................................................63 Error information...............................................................................................................64 LPI information (lens information).....................................................................................66 Preset playbachttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03k................................................................................................................67 AWB result........................................................................................................................68

sequences...................................................................................................................63

. Camera information batch acquisition.............................................................................................69 6. Error return......................................................................................................................................73 &lt;Appendix&gt;............................................................................................................................................75

. Introduction

manual describes the over TCP/IP Control Protocohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03l specifications which are applicable when the AW-HE50 HD integrated camera is operated using Ethernet.

consists of three main sections, namely, camera and pan-tilt head control, camera information update notifications and error return.

. Configuration outline

manual has the following general configuration.

① Camera and pan-tilt head control

is possible to control the pan, tilt and white balance adjustments.

is also possible to acquire the gain and other camera information by initiating queries.

various functions are employed for the operations with the camera using HTTP which is the host protocol of TCP.

further details, refer to chapter 3.  ② Camera information update notification

local terminal is notified of the values of the gain and other settings which have been changed at another terminal or other terminals so that it can acquhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ire the camera information.

feature is useful when one camera is controlled by a multiple number of terminals, and when the setting for enabling update notifications to be received has been established, the information which has been changed by other terminals can be acquired. For further details, refer to chapter 4.  ③ Camera information batch acquisition

camera information can be acquired in batch form.  Since there is no need to query each and every camera information item when this feature is used, the feature is useful when all the camera information is required such as at startup. For further details, refer to chapter 5.

④ Error return

error — whether ER1, ER2 or ER3 — is returned when an error has been generated by a command in ① above or when the AWB result contains an error. For further details, refer to chapter 6.

. Camera and pan-tilt head control

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03iven below are the external interfaces which are used when operating the AW-HE50 camera using Ethernet.

chapter presents the following details.

① Pan-tilt head control

which controls the pan-tilt head unit

② Camera control

which is related to the lens control of the camera unit and the image adjustments

.1. Pan-tilt head control

below is the command format which is used to control the pan-tilt head when the AW-HE50 camera is operated and which accords with the HTTP1.0 communication specifications.  For details on the HTTP messages, refer to &lt;Appendix&gt;.

[Command format] [Send]

://[IP Address]/cgi-bin/aw_ptz?cmd=[Command]&amp;res=[Type]

:

Address&#183;&#183;&#183;&#183;&#183;&#183;IP address of camera at connection destination

&#183;&#183;&#183;&#183;&#183;&#183;&#183;Details given in “Command” http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03column in the command tables below Type&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;Fixed at “1”

[Receive]

OK “Command”  Where:

&#183;&#183;&#183;&#183;&#183;&#183;&#183;Response value of each command; set in the HTTP message body

: Pan/tilt (Stop)

[Send]

://192.168.0.10/cgi-bin/aw_ptz?cmd=#PTS5050&amp;res=1

[Receive]

OK “pTS5050”

※In some cases, it may be necessary for “#” to be converted to “#” by ASCII conversion. http://192.168.0.10/cgi-bin/aw_ptz?cmd=#PTS5050&amp;res=1

below is the communication sequence which accords with the command format presented on the previous page.

the communication sequence of the errors generated in response to commands which have been sent, refer to “6. Error return”.

[Sequence]

“PC1” is the control terminahttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03l in the sequence below. Example: Pan/tilt (Stop) control

-HE50 IP Address = 192.168.0.10 Command = PTS5050

control to stop the pan-tilt operation is exercised from PC1.  [200 OK “pTS5050”] is returned as the response from the AW-HE50.

control command and query command are available as the pan-tilt head control commands. Given below is the command sequence.

[此处图片未下载成功]

. 3.1-1  Sequence of pan-tilt head control

must be borne in mind that communication with the camera is subject to some restrictions. These restrictions are as follows.

[Restrictions]

. When using the pan-tilt head control commands, send the commands with a gap of 130 ms between

command.  Given below is the sequence.

[此处图片未下载成功]

. 3.1-2  Restrictions

. The number of sessions during which the camera can http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03be accessed simultaneously is as follows.

) Maximum number of HTTP sessions: 72

) Number of terminals which can receive update notifications at the same time: 5

. Keep-Alive cannot be set with HTTP connections.

and disconnect are performed each time a command is sent or received. When the AW-RP50 is connected, it is counted as one unit.

.1.1. Power ON/OFF

commands enable the power ON/OFF of the AW-HE50 to be controlled and the current power ON/OFF statuses to be acquired.

3.1.1.  Power ON/OFF

name Category Command Setting Remarks

ON/OFF Data] 0 Power OFF  control command f Power OFF

Power ON n Power ON

]    Power ON/OFF None   query command 0 Power OFF  Data]

Power OFF 1 Power ON 2 Power ON

of use) Power ON [Control] PC → AW-HE50

://192http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03.168.0.10/cgi-bin/aw_ptz?cmd=#O1&amp;res=1 [Response] AW-HE50 → PC 200 OK “p1”

.1.2. Installation position

commands enable the AW-HE50 installation method (stand-alone or suspended) to be controlled and the current installation information to be acquired.

3.1.2.  Installation position

name Category Command Setting Remarks

position Data] 0 Desktop  control command 1 Hanging

]

position Data] None   query command 0 Desktop  Data]

Hanging

of use) Installation position: Desktop [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#INS0&amp;res=1 [Response] AW-HE50 → PC 200 OK “iNS0”

.1.3. Pan/tilt

commands enable the pan and tilt of the pan-tilt head of the AW-HE50 to be controlled and the current position information and operating speehttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03d to be acquired.

3.1.3.  Pan/tilt

name Category Command Setting Remarks

/tilt Data1][Data2][Data1] [Data1]Pan Pos

control command 0000

8000

FFFF

[Data2] [Data2]Tilt Pos

0000

8000

FFFF

][Data2]    Pan/tilt position None   query command  Data1][Data2] [Data1] [Data1]Pan Pos

0000

8000

FFFF

[Data2] [Data2]Tilt Pos

0000

8000

FFFF

(pan/tilt) Data] 01 Left Max. Speed

control command to to

Left Min. Speed

Stop 50

Right Min. Speed to to 99 Right Max. Speed

]     Data] 01 Down Max. Speed Tilt speed to be

to thttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03o

Down Min. Speed 50 Tilt Stop 51 UP Min. Speed to to 99 UP Max. Speed

]

name

value [Data1] 01 to 49 50 51 to 99

[Data2] 01 to 49 50 51 to 99

[Data1]

Max. Speed to

Min. Speed Pan Stop

Min. Speed to

Max. Speed [Data2]

Max. Speed to

Min. Speed Tilt Stop

Min. Speed to

Max. Speed

[Data1]

speed control[Data2]

speed control

][Data2]

][Data2]

of use)

Camera control PAN = 7FFF, TILT = 7FFF (Home position) [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#APC7FFF7FFF&amp;res=1 [Response] AW-HE50 → PC 200 OK “aPC7FFF7FFF”

Pan speed control, max. speed to the right [Control] PC → AW-HE50

://192.168.0.10/cgi-bihttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03n/aw_ptz?cmd=#P99&amp;res=1 [Response] AW-HE50 → PC 200 OK “pS99”

Tilt speed control, max. speed downward [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#T01&amp;res=1 [Response] AW-HE50 → PC 200 OK “tS01”

Pan/tilt speed control, max. speed to the left, max. speed upward [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#PTS0199&amp;res=1 [Response] AW-HE50 → PC 200 OK “pTS0199”

.1.4. Movement range limit ON/OFF

commands enable the movement range settings (limiter settings) for the pan and tilt of the AW-HE50 and the information of the current movement range limits to be acquired. Up, down, left and right limits can be set.

3.1.4.  Movement range limit ON/OFF

name Category Command Setting Remarks

directions in Movement range limit Data1][Data2][Data1] [Data1]

the movement ON/OFF http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e031 Up

is to be limited Down control command 2

controlled, and Left 3

set or release is 4 Right

.

[Data2] [Data2]

[Data1]

Release Control in the 1 Set movement range limit

[Data2]

set/release   Data1][Data2]

direction in which  Data] 1 Up

movement range 2 Down

to be limited is 3 Left

. 4 Right

※Operation toggles between set and release.

set/release  Data] 0 Release

Set

Command name

value 1 2 3 4

[Data1] 1 2 3 4

[Data2] 0 1

Up Down Left Right [Data1] Up Down Left Right [Data2] Release Set

range limit Data] ON/OFF

command

][Data2]

[Data1]

in the

range limit direction [Data2http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03]

set/release

of use)

Setting the movement range limit in the upward direction [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#LC11&amp;res=1 [Response] AW-HE50 → PC 200 OK “lC11”

Releasing the movement range limit in the upward direction [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#LC10&amp;res=1 [Response] AW-HE50 → PC 200 OK “lC10”

Setting/releasing the movement range limit in the upward direction [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#L1&amp;res=1 [Response] AW-HE50 → PC 200 OK “l0”

.1.5. Lens operations 3.1.5.1. Zoom

commands control the zooming (between Wide and Tele) of the AW-HE50 lens and enable the current zoom position and zooming speed to be acquired.

which control the zooming are also described in section “3.2.1.1. Zoom” of http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03“3.2. Camera control”.

3.1.5.1.  Zoom

name Category Command Setting Remarks

(position Data] 555 Wide   control) to to control command FFF Tele  Data]     Data] 001 Wide

to 999 Tele

]    Zoom position None   query command Data] 555 Wide

to FFF Tele “---” Power OFF

(speed control) Data] 01 Wide Max. Speed Zooming speed to be

control command to to

Wide Min. Speed

Stop 50

Tele Min. Speed to to 99 Tele Max. Speed

]

of use)   Zoom: Tele

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AXZFFF&amp;res=1 [Response] AW-HE50 → PC 200 OK “axzFFF”

Zoom: Tele

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AYZ999&amp;res=1 [Response] AW-HE50 → PC 200 OK “ayz999”

Speed control, max. zooming spehttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ed in Wide direction [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#Z01&amp;res=1 [Response] AW-HE50 → PC 200 OK “zS01”

.1.5.2. Focus

commands control the focusing (between Near and Far) of the AW-HE50 lens and enable the current focus position and focus adjustment speed to be acquired.

which control the focusing are also described in section “3.2.1.2. Focus” of “3.2. Camera control”.

3.1.5.2.  Focus

name Category Command Setting Remarks

Invalid when auto Focus (position Data] 555 Near

is ON (ER3 is control) to to

) control command FFF Far

]

Invalid when auto  Data] 001 Near

is ON (ER3 is to to

) 999 Far

]

position None

command  555 Near  Data]

to FFF Far “---” Power OFF

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03s (speed control) Data] 01 Near Max. Speed  Focusing speed to

controlled control command to to

Near Min. Speed  Invalid when auto

is ON (ER3 is Focus Stop 50

) 51 Far Min. Speed

to 99 Far Max. Speed

]    Auto focus ON/OFF Data] 0 OFF (Manual)  control command 1 ON (Auto)

]

focus ON/OFF None   query command 0 OFF (Manual)  Data]

ON (Auto)

of use)  Focus: Near

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AXF555&amp;res=1 [Response] AW-HE50 → PC 200 OK “axf555”

Focus: Near

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AYF001&amp;res=1 [Response] AW-HE50 → PC 200 OK “axf001”

Speed control, max. focusing speed in Far direction [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#F99&amp;res=1 [Response] AW-HEhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e0350 → PC 200 OK “fS99”

Auto focus, auto focus start [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#D11&amp;res=1 [Response] AW-HE50 → PC 200 OK “d11”

.1.5.3. Iris

commands control the iris (between Close and Open) of the AW-HE50 lens and enable the current iris position to be acquired.

addition, they enable Auto/Manual control of the iris and the current iris Auto/Manual statuses to be acquired.

which control the iris are also described in section “3.2.1.3. Iris” of “3.2. Camera control”.

3.1.5.3.  Iris

name Category Command Setting Remarks

position  [Data] 01 Iris Close  control command to to

Iris Open

]      [Data] 555 Iris Close

to FFF Iris Open

[Data]      [Data] 001 Iris Close

to 999 Iris Open

[Data]    Iris position   Authttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03o/Manual  [Data1] [Data2]  [Data1][Data1] query command 555 Iris Close

to

Open FFF

“---” Power OFF [Data2][Data2] 0 Manual Iris 1 Auto Iris

iris ON/OFF Data] 0 Manual Iris  control command 1 Auto Iris

]

iris ON/OFF   query command 0 Manual Iris  Data]

Auto Iris

of use)  Iris: Open

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#I99&amp;res=1 [Response] AW-HE50 → PC 200 OK “iC99”

Iris: Close

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AXI555&amp;res=1 [Response] AW-HE50 → PC 200 OK “axi555”

Iris: Open

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#AYI999&amp;res=1 [Response] AW-HE50 → PC 200 OK “axi999”

Auto iris: ON

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#D31&amp;res=1 [Respohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03nse] AW-HE50 → PC 200 OK “d31”

.1.6. Lens information notification ON/OFF

commands control the ON/OFF of the AW-HE50 lens information notification and enable current lens information notification ON/OFF status to be acquired.

3.1.6.  Lens information notification ON/OFF

name Category Command Setting Remarks

: Information is Lens information Data] 0 OFF

posted. 1 ON notification

:  Information is control command Data]

.  Lens information  None

OFF:  Information is 0 OFF Data] query command not posted. 1 ON

:  Information is

.

of use) Lens information notification: ON [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#LPC1&amp;res=1 [Response] AW-HE50 → PC 200 OK “lPC1”

.1.7. Preset

commands rhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03egister and play back the presets of the AW-HE50 and enable the preset number last played back to be acquired.

3.1.7.  Preset

name Category Command Setting Remarks

(register) Data] 00 Preset 01  control command  to to

Preset 100

]    Preset (playback) Data] 00 Preset 01  control command  to to

Preset 100

]

for preset Preset number None

last played query command

] 00 Preset 01

to 99 Preset 100

※After the presets have all been played back, the completion notification is sent in the “q**” format. For details, refer to “4.4.4. Preset playback”.

of use)

Registering a setting in preset 08 [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#M07&amp;res=1 [Response] AW-HE50 → PC 200 OK “s07”

Playing back preset 12 [Chttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ontrol] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#R11&amp;res=1 [Response] AW-HE50 → PC 200 OK “s11”

.1.8. Tally

commands exercise enable/disable control over the tally input of the AW-HE50 and enable the current tally input enable/disable statuses to be acquired.

addition, they exercise tally ON/OFF control over the AW-HE50.

3.1.8.  Tally

name Category Command Setting Remarks

input Data] 0 Disable  enable/disable 1 Enable control command Data]    Tally input None   enable/disable 0 Disable  Data] query command 1 Enable Tally ON/OFF Data] 0 Tally OFF  control command 1 Tally ON  Data]    Tally ON/OFF    query command Data] 0 Tally OFF   1 Tally ON

of use)

Tally input (enable/disable): Enable [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#TAE1&amp;res=1 [Response]http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 AW-HE50 → PC 200 OK “tAE1”

Tally ON

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#DA1&amp;res=1 [Response] AW-HE50 → PC 200 OK “dA1”

.1.9. Zoom position-linked pan/tilt speed adjustment ON/OFF

commands exercise ON/OFF control over the zoom position-linked pan/tilt speed adjustments of the AW-HE50 and enable the current ON/OFF statuses to be acquired.

the lens is zoomed toward Tele, the pan/tilt movement is set to the low speed.

3.1.9.  Zoom position-linked pan/tilt speed adjustment ON/OFF

name Category Command Setting Remarks

position-linked Data] 0 OFF  pan/tilt speed 1 ON adjustment ON/OFF control command    Data] Zoom position-linked None   pan/tilt speed 0 OFF  Data] adjustment 1 ON query command

of use)

Zoom position-linked pan/tilt speed adjustment: ON [Conhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03trol] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_ptz?cmd=#SWZ1&amp;res=1 [Response] AW-HE50 → PC 200 OK “sWZ1”

.2. Camera control

below is the command format which is used to control the camera unit when the AW-HE50 camera is operated and which accords with the HTTP1.0 communication specifications. For details on the HTTP messages, refer to &lt;Appendix&gt;.

[Command format] [Send]

://[IP Address]/cgi-bin/aw_cam?cmd=[Command]&amp;res=[Type]

:

Address&#183;&#183;&#183;&#183;&#183;&#183;IP address of camera at connection destination

&#183;&#183;&#183;&#183;&#183;&#183;&#183;Details given in “Command” column in the command tables below Type&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;Fixed at “1” (and “0” for the “OWS” command)

[Receive]

OK “Command” Where:

&#1http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e0383;&#183;&#183;&#183;&#183;&#183;&#183;Response value of each command; described in the HTTP message body.

: Focus setting = Auto

[Send]

://192.168.0.10/cgi-bin/aw_cam?cmd=OAF:0&amp;res=1 [Receive] The response is the HTTP response. 200 OK “OAF:0”

below is the sequence used when communication has been performed in accordance with the command format described on the previous page.

the sequence when errors have been generated in response to commands, refer to “6. Error return”.

[Sequence]

“PC1” is the control terminal in the sequence below. Example: Focus setting = Auto

-HE50 IP Address = 192.168.0.10 Command = OAF:1

focus control is performed from PC1, and [200 OK “OAF:1”] is returned as the response. Both a control command and query command are available as the camera control commands. Given below is the command sequence.://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03par

[此处图片未下载成功]

. 3.2-1  Camera control command sequence

following restrictions should be noted when using these commands. These restrictions are as follows.

[Restrictions]

sending the camera control commands, send the commands with a gap of 130 ms between each command.

below is the command sequence.

[此处图片未下载成功]

. 3.2-2  Restrictions

.2.1. Lens operations 3.2.1.1. Zoom

commands control the zooming (between Wide and Tele) of the AW-HE50 lens.

which control the zooming are also described in section “3.1.5.1. Zoom” of “3.1. Pan-tilt head control”.

3.2.1.1.  Zoom

name Category Command Setting Remarks

lens zooms Zoom

Tele. control command

lens zooms

Wide.

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 stop control

speed to be Zoom Data] 0 Slow

(HZT, (speed-designated) to to

speed control)control command 9 Fast

]

of use)  Zoom Tele

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=HZT&amp;res=1 [Response] AW-HE50 → PC 200 OK “HZT”

Maximum zoom speed [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=LZS:9&amp;res=1 [Response] AW-HE50 → PC 200 OK “LZS:9”

.2.1.2. Focus

commands control the AW-HE50 focusing.

also exercise Auto/Manual control of the focusing and one-touch auto focus control.

which control the focusing are also described in section “3.1.5.2. Focus” of “3.1. Pan-tilt head control”.

3.2.1.2.  Focus

name Category Command Setting Remarks

Data] 0 Manual  Auto/Manual 1 Auto contrhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ol command    Data] Focus None   Auto/Manual 0 Manual  Data] query command 1 Auto

(end control)

Near control command

of movement

Far

control

speed to Focus (speed Data] 0 Slow

controlled designated) to to

(HFF, HFN speed control command 9 Fast

)  Data]

-touch auto focus Data] One-touch auto

ON control control command

]

of use)

Focus (Auto/Manual): Auto [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OAF:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OAF:0”

Focus: Near

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=HFN&amp;res=1 [Response] AW-HE50 → PC 200 OK “HFN”

Maximum focus speed [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=LFS:9&amp;res=1 [Resphttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03onse] AW-HE50 → PC 200 OK “LFS:9”

Execution of one-touch auto focus control [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:69:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:69:1”

.2.1.3. Iris

commands control the iris (between Close and Open) of the AW-HE50 lens and enable the current iris position to be acquired.

also exercise iris Auto/Manual control and check the iris Auto/Manual statuses.

addition, they enable the contrast level to be set in ten steps and the setting to be verified.

which control the iris are also described in section “3.1.5.3. Iris” of “3.1. Pan-tilt head control”.

name Iris Auto/Manual control command

Auto/Manual query command Contrast level control command

3.2.1.3.  Iris

Command

] 0

]http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03  None

Data]

] 64

A to 6350 to 5946 to 4F3C to 4532 to 3B28 to 311B to 2714 to 1A0A to 1300 to 09

Manual Auto   Manual Auto  5  4  3  2  1 0  1  2  3  4  5

level query command

] Data]

A to 6350 to 5946 to 4F3C to 4532 to 3B28 to 311B to 2714 to 1A0A to 1300 to 09000 to 3FF

5  4  3  2  1 0  1  2  3  4  5 Close to Open

While “----” is displayed for

Level on the OSD menu, the setting is accepted but it is not reflected in the images. The

is reflected in the images when the “----” display is released.  Contrast level control (Auto)

Contrast level control (Auto)

volume

command

volume

command

]

volume control (Manual)

volume status request (Manual)

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03a] Data]

000 to 3FF

00 to FF

to Open  Close to Open

]

volume status request

of use)  Auto iris: ON

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=ORS:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “ORS:1”

Iris: Open

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=ORV:3FF&amp;res=1 [Response] AW-HE50 → PC 200 OK “ORV:3FF”

Contrast level: 0

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSD:48:30&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSD:48:30”

.2.2. Color bar ON/OFF

commands exercise ON/OFF control over the color bars of the AW-HE50 and enable the current settings to be acquired.

3.2.2.  Color bar ON/OFF

name Category Command Setting Remarks

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03alue

bar ON/OFF Data] 0 Camera  control command 1 Color Bar  Data]    Color bar ON/OFF None   query command 0 Camera  Data]

Color Bar

of use) Color bar: ON [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=DCB:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “DCB:1”

.2.3. Scene file setting

commands specify the scene files of the AW-HE50 and enable the settings of the currently selected scene file to be acquired.

3.2.3.  Scene file setting

name Category Command Setting Remarks

file Data] 1 Manual1  control command 2 Manual2

Manual3 4 FullAuto

]    Scene file None   query command 0 Manual1  Data]

Manual2 2 Manual3 3 FullAuto

of use) Scene file: Manual1 [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=XSF:1&amhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03p;res=1 [Response] AW-HE50 → PC 200 OK “XSF:1”

.2.4. Shutter mode setting

commands control the shutter of the AW-HE50 and enable the currently set shutter mode to be acquired.

3.2.4.  Shutter mode setting

name Category Command Setting Remarks

Disabled at the Shutter Data] 0 Shutter OFF

setting control command 3 1/100(60Hz)

(ER3 is returned).

/120(50Hz)  When auto iris is ON, 5 1/250 the setting is 6 1/500 accepted but it is not

in the 1/1000 7

. The setting 8 1/2000

reflected in the

1/4000 images when auto A 1/10000 iris is changed from B Synchro-Scan ON to OFF.

]    Shutter None   query command  0 Shutter OFF Data]

1/100(60Hz)

/120(50Hz)

1/250 6 1/500 7 1/1000 8 1/2000 9 1/4000

/10000 A

Synchro-Scan

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ynchro scan Data] 001 60.24Hz(60Hz)

setting

command  50.20Hz(50Hz) (ER3 is returned).

to  When auto iris is ON,

setting is

but it is not

646.21Hz(60Hz) reflected in the  538.51Hz(50Hz) images. The setting

reflected in the

when auto iris is changed from ON to OFF.  While “----” is displayed for

/Synchro on the OSD menu, the setting is accepted but it is not reflected in the images. The setting is reflected in the images when the “----” display is released.

scan query command

OMS:[Data] Data]

to  255

.24Hz(60Hz) 50.20Hz(50Hz) to

.21Hz(60Hz) 538.51Hz(50Hz)

of use)  Shutter: 1/500

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSH:6&amp;res=1 [Response] AW-HE50 → PC 200 http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03OK “OSH:6”

Synchro scan: 60.24Hz [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OMS:001&amp;res=1 [Response] AW-HE50 → PC 200 OK “OMS:001”

.2.5. Frame mix setting

commands enable the frame mixing of AW-HE50 to be set and the current settings to be acquired.

3.2.5.  Frame mix setting

name Category Command Setting Remarks

Disabled at the Frame mix Data] 00 OFF

setting control command 06 6dB

(ER3 is returned).

C 12dB  When auto iris is ON, 12 18dB the setting is 80 Auto accepted but it is not

in the

.  The setting is reflected in the images when auto iris is changed from ON to OFF.

mix

command

] Data]

06 0C 12 80 00 01 02 03  00 01 02 03

6dB 12dB 18dB Auto 0dB 6dB 12dB 18dB  0dB 6dB 12dB http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e0318dB

frame mix value

command

frame mix value

command

]

Disabled at the FullAuto setting (ER3 is returned).  Maximum frame mix value control (Auto)

] Data]

of use)    Frame mix: 12dB

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSA:65:0C&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSA:65:0C”

Maximum frame mix value: 18dB [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:74:03&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:74:03”

.2.6. Gain setting

commands enable the gain settings of the AW-HE50 to be established and the current settings to be acquired.

model : AW-HE50 Method : GET

3.2.6.  Gain setting

name Category Command Setting Remhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03arks

Disabled at the Gain Data] 08 0dB

setting control command 0B 3dB

(ER3 is returned).0E 6dB

9dB 14 12dB

dB 17

dB 1A

AGC On

]    Gain None   query command 08 0dB  Data]

B 3dB 0E 6dB

dB 11

12dB 17 15dB 1A 18dB 80 AGC On

Disabled at the Maximum gain value Data] 01 6dB

setting control command 02 12dB

(ER3 is returned).03 18dB

Maximum gain value control (Auto)

]    Maximum gain value    query command  Disabled at the 01 6dB

setting 02 12dB

(ER3 is returned).03 18dB

Maximum gain value control (Auto)

of use)  Gain: 3dB

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OGU:0B&amp;res=1 [Response] AW-HE50 → PC 200 OK “OGU:0B”

Maximum gain: 18dB

[Control] PC → AW-HE50

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03p://192.168.0.10/cgi-bin/aw_cam?cmd=OSD:69:03&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSD:69:03”

.2.7. Chroma level setting

commands enable the chroma level of the AW-HE50 to be set and the current settings to be acquired.

3.2.7.  Chroma level setting

name Category Command Setting Remarks

Disabled at the Chroma level Data] 00  3

setting control command 01  2

(ER3 is returned). 02  1

0 04  1 05  2 06  3

]    Chroma level None   query command 00  3  Data]

2 02  1

03

1 05  2 06  3

of use)  Chroma level: 0

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OCG:03&amp;res=1 [Response] AW-HE50 → PC 200 OK “OCG:03”

.2.8. AWB setting

commands select the AWB mode of the AW-HE50, execute AWB andhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 enable the current AWB mode status to be acquired.

3.2.8.  AWB setting

name Category Command Setting Remarks

(AWC) is AWB (AWC)

. execution

command

execution Data] 0 OFF

status 1 ON display ON/OFF    Data] control command

execution None

status  Data] 0 OFF display ON/OFF 1 ON query command

Disabled at the AWB (AWC) mode Data] 0 ATW

setting control command 1 AWB A

(ER3 is returned).2 AWB B

ATW

] 0 ATW

AWB A 3 AWB B

(AWC) mode None   query command 0 ATW  Data]

AWB A 3 AWB B

※The results of the AWB (AWC) execution are posted by the update notification. For details, refer to “4.4.5. AWB result”.

of use)

AWB (AWC) execution [Control] PC → AW-HE50

://192http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03.168.0.10/cgi-bin/aw_cam?cmd=OWS&amp;res=0 [Response] AW-HE50 → PC None

AWB (AWC) execution underway status display: ON [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSA:88:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSA:88:1”

AWB (AWC) mode: ATW [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OAW:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OAW:0”

.2.9. Detail setting

commands control the detail of the AW-HE50 and enable the current settings to be acquired.

3.2.9.  Detail setting

name Category Command Setting Remarks

Disabled at the Detail Data] 0 OFF

setting control command 1 LOW

(ER3 is returned). 2 HIGH

]    Detail None   query command 0 OFF  Data]

LOW 2 HIGH

of use) Detail: LOW [Control] PC → AW-HE50

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03://192.168.0.10/cgi-bin/aw_cam?cmd=ODT:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “ODT:1”

.2.10. Flesh Tone Mode setting

commands control the flesh tone mode of the AW-HE50 and enable the current settings to be acquired.

3.2.10.  Flesh Tone Mode setting

name Category Command Setting Remarks

Disabled at the Flesh Tone Mode Data] 0 OFF

setting control command 1 LOW

(ER3 is returned).3 HIGH

]    Flesh Tone Mode None   query command 0 OFF  Data]

LOW 3 HIGH

of use) Flesh Tone Mode: HIGH [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:32:3&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:32:3”

.2.11. Digital noise reduction (DNR) setting

commands control the digital noise reduction (DNR) of the AW-HE50 and enable the current setthttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ings to be acquired.

3.2.11.  Digital noise reduction (DNR) setting

name Category Command Setting Remarks

Disabled at the Digital noise Data] 00 OFF

setting reduction (DNR) 01 LOW

(ER3 is returned).control command 02 HIGH

]    Digital noise None   reduction (DNR) 00 OFF  Data] query command 01 LOW

HIGH

of use) Digital noise reduction (DNR): HIGH [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSD:3A:02&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSD:3A:02”

.2.12. Pedestal setting

commands control the pedestal of the AW-HE50 and enable the current settings to be acquired.

3.2.12.  Pedestal setting

name Category Command Setting Remarks

Disabled at the Pedestal Data] 000  150

settinhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03g control command to to

(ER3 is returned). 096 0

The data value to to

by 15 is 12C  150

.   Data]

None

command 000  150 Data]

by 15 is to to

. 096 0

to 12C  150

Disabled at the Pedestal Data] 00  30

setting control command to to

(ER3 is returned). 1E 0

The data value to to

by 3 is set.3C  30

]

None

command  The data value 00  30 Data]

by 3 is set.to to

E 0 to to 3C  30

of use)  Pedestal:  10

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OTP:000&amp;res=1 [Response] AW-HE50 → PC 200 OK “OTP:000”

Pedestal:  10

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OTD:3C&amp;res=1 [Response] AW-HE50 → PC 200 OK “OTD:3C”

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03par3.2.13. DRS setting

commands control the DRS of the AW-HE50 and enable the current settings to be acquired. There are three setting items: DRS, gamma type and gamma level.

3.2.13.  DRS setting

name Category Command Setting Remarks

Disabled at the DRS Data] 0 OFF

setting control command 1 LOW

(ER3 is returned).

HIGH

]    DRS None   query command 0 OFF  Data]

LOW 3 HIGH

type Data] 0 OFF

setting

command 1 NORMAL (ER3 is returned).

CINEMA  When the DRS is in any

except OFF, the

is accepted but it is not reflected in the images. The setting is reflected in the

when DRS is changed from the mode which is not OFF to OFF.

type query command

] Data]

1 2 00 01 02

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03

CINEMA LOW MID HIGH

level control command

]

setting (ER3 is returned). When the DRS is in any

except OFF, the setting is accepted but it is not reflected in the images. The setting is reflected in the

when DRS is changed from the mode which is not OFF to OFF.  When the DRS is in any mode except OFF and any setting except Normal is established for the gamma type, the setting is accepted but it is not reflected in the images. The setting is reflected in the images when DRS is changed to OFF and the gamma type is changed to Normal.

level query command

] Data]

01 02

MID HIGH

of use)  DRS: OFF

[Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:33:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:33:0”

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 Gamma type: NORMAL  [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:72:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:72:1”

Gamma level: MID [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSD:50:01&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSD:50:01”

.2.14. Backlight compensation setting

commands exercise ON/OFF control over the backlight compensation of the AW-HE50 and enable the current settings to be acquired.

3.2.14.  Backlight compensation setting

name Category Command Setting Remarks

Disabled at the Backlight Data] 0 OFF

setting compensation 1 ON

(ER3 is returned).control command

When ON is set for auto iris and Auto is set for Frame Mix and AGC On is set for Gain, the setting is accepted but it is not reflected in the images. The

ishttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 reflected in the images when auto iris is changed from ON to OFF, or Frame Mix or Gain is changed to Manual.

]    Backlight None   compensation 0 OFF  Data] query command 1 ON

of use)

Backlight compensation: OFF [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:73:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:73:0”

.2.15. Genlock setting

commands exercise genlock control over the AW-HE50 and enable the current settings to be acquired.

setting items include horizontal sync phase, subcarrier sync phase (coarse) and subcarrier sync phase (fine).

3.2.15.  Genlock setting

name Category Command Setting

sync phase Data] 000  206 control command to to

0 to to 3FF  49

]   Horizontal sync phase None  query command

] 000  206://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03rto 338 0 to to 3FF  49

sync Data] 0 90&#176; phase (coarse) 1 180&#176; control command 2 270&#176;

0&#176;

]   Subcarrier sync None  phase (coarse)

] 0 90&#176; query command

180&#176;

&#176; 2

&#176; 3

45&#176; 6 135&#176; 7 225&#176;

&#176; 8

127 Subcarrier sync Data] 000

phase (fine) to

command 007  127

126 008

to 200 0

to

126 3FB

FC  127 to to

127 3FF

]   Subcarrier sync None  phase (fine)

]  127 000 query command

to

127 007

126 to to 200 0 to to 3FB  126 3FC  127 to to 3FF  127

This command has no

with the H model.

This command has no effect with the H model.

This command has no effect with the H model.

http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03This command has no effect with the H model.

This command has no effect with the H model.

This command has no effect with the H model.

of use)

Horizontal sync phase:  49 [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OHP:3FF&amp;res=1 [Response] AW-HE50 → PC 200 OK “OHP:3FF”

Subcarrier sync phase (coarse): 90&#176; [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSC:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSC:0”

Subcarrier sync phase control (fine):  127 [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSN:3FF&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSN:3FF”

.2.16. Output setting

commands control the output settings of the AW-HE50 and enable the current settings to be acquired.

setting items include format, down-conversion mode anhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03d HDMI color components.

3.2.16.  Output setting

name Category Command Setting Remarks

Data] 01 720/59.94p (59.94Hz)  Data values with

field control command 02 720/50p (50Hz)

are 04 1080/59.94i (59.94Hz)

(the ER3 05 1080/50i (50Hz)

is 0b 480/59.94i (59.94Hz)

).

d 576/50i (50Hz)

command

] Data]

02 04 05 0b 0d 0 1 2  0 1 2 0 1 2 3

/59.94p (59.94Hz)

/50p (50Hz)

/59.94i (59.94Hz) 1080/50i (50Hz)

/59.94i (59.94Hz) 576/50i (50Hz) SideCut Squeeze LetterBOX

Squeeze LetterBOX RGB-NOR RGB-ENH YCbCr422 YCbCr444

-conversion mode

command

-conversion mode

command HDMI color component

command

color chttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03omponent

command

]

] Data]

]

This command

no effect with the S model.

no effect with the S model.

]

]

1 2 3 RGB-NOR RGB-ENH YCbCr422 YCbCr444

of use)

Format: 720/59.94p [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSA:87:01&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSA:87:01”

Down-conversion mode: Squeeze [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:20:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:20:1”

HDMI color components: RGB-NOR [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:68:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:68:0”

.2.17. Preset playback range setting

commands control the playback range when the presets of the AW-HE50 are to be phttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03layed back and enable the current settings to be acquired.

3.2.17.  Preset playback range setting

name Category Command Setting Remarks

playback Data] 0 Mode A  range 1 Mode B control command 2 Mode C  Data]    Preset playback None   range 0 Mode A  Data] query command 1 Mode B

Mode C

of use) Preset playback range: Mode A [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:71:0&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:71:0”

.2.18. Digital zoom ON/OFF setting

commands control the digital zoom ON/OFF of the AW-HE50 and enable the current settings to be acquired.

3.2.18.  Digital zoom ON/OFF setting

name Category Command Setting Remarks

zoom ON/OFF Data] 0 DISABLE  control command 1 ENABLE  Data]    Digital zoom ONhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03/OFF None   query command 0 DISABLE  Data]

ENABLE

of use) Digital zoom: ON [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=OSE:70:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSE:70:1”

.2.19. Camera information acquisition

commands enable the current camera information of the AW-HE50 to be acquired.

3.2.19.  Camera information acquisition

name Category Command Setting Remarks

number None

command Model number of AW-HE50 Data]

Camera None

Data]   software version microcontroller query command software version

: V01.28

of use)

Model number acquisition [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=QID&amp;res=1 [Response] AW-HE50 → PC 200 OK “OID:AW-HE50”

Camerahttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 microcontroller software version acquisition [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=QSV&amp;res=1 [Response] AW-HE50 → PC 200 OK “OSV:V01.00”

.2.20. OSD menu

commands exercise control over the OSD menu of the AW-HE50 and enable the current settings to be acquired.

3.2.20.  OSD menu

name Category Command Setting Remarks

camera OSD OSD menu OFF/ON Data] 0 Menu OFF

is turned ON or control command 1 Menu ON

.   Data]

menu OFF/ON None

command  0 Menu OFF Data]

Menu ON

value is MENU switch ON canceled. control command

. ITEM switch ON

command

cursor moves up YES switch ON

(the value is control command

). The cursor moves NO switch ON

(the value is control command

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03cremented).

of use) OSD menu: ON [Control] PC → AW-HE50

://192.168.0.10/cgi-bin/aw_cam?cmd=DUS:1&amp;res=1 [Response] AW-HE50 → PC 200 OK “DUS:1”

. Camera information update notification

AW-HE50 comes with a camera information update notification function that provides notification of statuses and information.

this chapter, the phrase “camera information update notification” will be abbreviated to “update notification”.

the completion of preset playback and the results of the AWB execution are posted using the update notification function, settings must be established to enable the update notifications to be received before the function is used.

notification takes effect when one AW-HE50 camera is controlled by a multiple number of terminals. Once the settings have been established to enable the update notifications to be http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03received, it is then possible for any terminal to acquire the information which has been updated by other terminals.

.1. Procedure for receiving the update notifications

procedure for receiving the update notifications consists of two steps, namely, ① the update notification receive start step and ② the update notification receive end step, and each step is described below.

① Update notification receive start step

: When the IP address of the AW-HE50 camera is “192.168.0.10” and the update notifications are to be received at the port of the local terminal with port number “80”

://192.168.0.10/cgi-bin/event?connect=start&amp;my_port=80&amp;uid=50

※my_port … Number of port where update notifications are received (1 to 65535)

below is the sequence which is followed when receiving the update notifications is started.

[Update notification receive start sequenchttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03e]

update notification receive start command is sent from the terminal where the update notifications are to be received.

“204 No Content” is returned from the AW-HE50 camera which has received the command.

[此处图片未下载成功]

Fig. 4-1  Update notification receive start sequence

[Caution]

② Update notification receive end step

close the application of the client, the update notification receive end step must be taken without fail.

: When the IP address of the AW-HE50 camera is “192.168.0.10” and the reception of the update notifications is to be ended at the port of the local terminal with port number “80”

://192.168.0.10/cgi-bin/event?connect=stop&amp;my_port=80&amp;uid=50

※my_port … Number of port where update notifications are received (1 to 65535)

below is the sequence which is followed when receiving the update nohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03tifications is to be ended.

[Update notification receive end sequence]

update notification receive end command is sent from the terminal which has received the update notifications.

“204 No Content” is returned from the AW-HE50 camera which received the command.

[此处图片未下载成功]

. 4-2  Update notification receive end sequence

.2. Data format for update notifications

data received in the update notifications will be described next. Notification of updates is given by TCP protocol communication. A breakdown of the data received is given below.

[Receive data]

(22Byte)

(2Byte)

(4Byte)

notification information (Variable length: Max. 504 bytes)

(24Byte)

. 4-3  Receive data format

updated information is set in “Update notification information” of http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03the receive data format. The data received from the AW-HE50 has a variable length.

size of the update notification information is the value obtained by subtracting 8 bytes from the “Size” area setting.

“Update notification information” data length = “Size” － 8 bytes

updates of the AW-HE50 are described in the update notification information. The format used for the update notification information received from the AW-HE50 is given below.

[Update notification information format]

[CR][LF][Command][CR][LF]

※ [CR]: 0x0d, [LF]: 0x0a

1) Power ON

[CR][LF]p1[CR][LF] Example 2) Color bar: ON

[CR][LF]DCB:1[CR][LF]

.3. Setting change sequence

notifications are sent when the settings or statuses of the camera have been changed. Given below is an example of the update notification sequence.

.3.1. Changing thhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03e settings from a terminal

[Changing the settings from the local terminal]

the settings of the AW-HE50 have been changed from the local terminal with update notification receive already set, the changes are posted by an update notification.

the local terminal (PC1), the changes are also posted by an update notification separately from the response to the command.

[此处图片未下载成功]

. 4-4  Changing the settings from the local terminal

[Changing the settings from another terminal]

, when the settings of the AW-HE50 have been changed from another terminal (PC2), update notification receive has been set for the AW-HE50, the local terminal (PC1) is notified of the changes in the settings even when these changes have been made from another terminal.

an IP connection or serial connection is established for the AW-HE50, the other terminal (PC2) is notifiedhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 of the changes.

[此处图片未下载成功]

. 4-5  Changing the settings from another terminal

(Remarks)

the control commands have been received by the AW-HE50, update notifications are posted when the settings are changed. However, they are not posted when any of the following commands have been received.

① OSD menu

name Command OSD menu OFF/ON control command DUS:[Data] MENU switch ON control command DPG ITEM switch ON control command DIT YES switch ON control command DUP NO switch ON control command DDW

② Pan, tilt, zoom, focus and iris operation commands

&lt;Pan-tilt head control commands&gt;

name

/tilt control command

#APC[Data1][Data2] #P[Data] #T[Data]

#PTS[Data1][Data2] #AXZ[Data] #AYZ[Data] #Z[Data] #AXF[Data] #AYF[Data] #F[Data] #I [Data] #AXI [Data] #AYI [Data]

chttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ontrol command

control command

position control command

&lt;Camera control commands&gt;

name

control command

HZT HZW HZS

:[Data] HFN HFF HFS

:[Data] OSE:69:[Data] OSD:48:[Data] ORV:[Data]

control command

-touch auto focus control command Contrast level control command Iris volume control command

.3.2. Initialization using OSD menu

cases where the settings have been initialized by OSD menu operations of the AW-HE50, the update notifications in the table below are posted in sequence.

4-1

Remarks file (Auto/Manual) level scan mix OSD:69 Maximum gain value OSE:74 Maximum frame mix value level OAW AWB (AWC) mode OSE:32 Flesh Tone Mode OSD:3A Digital noise reduction (DNR) type level compensation OHP Horizontal sync phase OSC Subcarrierhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 sync phase (coarse) OSN Subcarrier sync phase (fine) mode OSE:68 HDMI color component position uPVS Pan preset speed OSE:71 Preset playback range zoom ON/OFF sWZ Zoom position-linked pan/tilt speed adjustment ON/OFF Auto/Manual OAZ Auto focus ON/OFF during zooming tAE Tally input enable/disable OSA:88 AWB execution underway status display ON/OFF control OSE:75 OSD off with tally

below is the sequence which is followed when the settings are initialized by OSD menu operations.

[Sequence of initialization by OSD menu operations]

cases where the settings of the AW-HE50 have been initialized from the OSD menu, the items whose settings were changed by initialization are posted in sequence as update notifications.

[此处图片未下载成功]

. 4-6  Initialization using OSD menu

.3.3. Scene file selection

scene files are selected, the update notifhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ications in the table below are posted in sequence.

4-2

Remarks file (Auto/Manual) level scan mix OSD:69 Maximum gain value OSE:74 Maximum frame mix value level OAW AWB (AWC) mode OSE:32 Flesh Tone Mode OSD:3A Digital noise reduction (DNR) type level compensation

below is the sequence which is followed when scene files are selected.

[Scene file selection sequence]

sequence below is followed when the scene file is changed to “Manual1.”

“XSF:1” is returned in the response to the scene selection command and the scene file change is completed, the settings changed by the change in the scene file are posted in sequence by update notifications.

[此处图片未下载成功]

. 4-7  Scene file selection

which differ from the sequences described on the previous pages will be given in the following pages.

://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03par4.4. Special sequences

notifications are sometimes sent at times other than when the settings or statuses of the camera have been changed.

cases are presented below.

.4.1. Version information notification

version information is posted in 60-second cycles. The information posted is given below.

4-3

Version information

below is the sequence which is followed when the version information is received.

[Sequence when the version information is received]

AW-HE50 sends the version information in 60-second cycles, and this information is received by terminals PC1 and PC2.

[此处图片未下载成功]

. 4-8  Sequence when the version information is received

.4.2. Error information

cases where the AW-HE50 has detected error information, the error informatiohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03n is posted in 30-second cycles.

the error has been avoided or not detected, the error information is not posted. Given below is the information which is posted.

4-4

rER[Error Code]

: Normal

: Motor Driver Error (operation status 2-7bit) 04: Pan Sensor Error (operation status 2-4bit) 05: Tilt Sensor Error (operation status 2-3bit) 06: Controller RX Over run Error 07: Controller RX Framing Error 08: Network RX Over run Error 09: Network RX Framing Error

: Controller RX Command Buffer Overflow 19: Network RX Command Buffer Overflow 21: System Error (operation status 2-6bit)  22: Spec Limit Over (2-0, 1, 3-6 or 7bit)  23: FPGA Config Error

: UniS communication Error

(dead/alive monitoring reset generated)

Code

below is the sequence which is followed when error information is received.

[Error informhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03ation receive sequence]

the AW-HE50 detects an error, it sends the error information to the terminals, and terminals PC1 and PC2 receive this information.

[此处图片未下载成功]

. 4-9  Sequence when error information is received

.4.3. LPI information (lens information)

cases where ON has been selected as the “3.1.6. Lens information notification ON/OFF” and changes have been made in the LPI information (lens information), the LPI information is posted in 300-millisecond cycles. Given below is the information which is posted.

4-5

Lens information

&#183;&#183;&#183;Zoom position

[ZZZ] [FFF] [III] FFF&#183;&#183;&#183;Focus position

&#183;&#183;&#183;&#183;&#183;&#183;Iris position

below is the sequence which is followed when changes in the LPI (lens) information are receivedhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03.

[此处图片未下载成功]

[Sequence when LPI information (lens information) is changed]

the AW-HE50 detects changes in the LPI (lens) information, the changed LPI (lens) information is sent to the terminals, and terminals PC1 and PC2 receive this information.

. 4-10  Sequence when LPI information is changed

.4.4. Preset playback

presets have been played back by the AW-HE50, notification that the preset playback has finished is posted as an update notification. The table below shows what is posted.

4-6

Remarks

of the preset which was

[numeral]

back

below is the sequence which is followed when presets are played back.

[Preset playback sequence]

is the sequence in which preset number 08 is played back.

“s07” is returned in the response to the cohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03mmand, and when the playback of preset number 08 is finished, “q07” is posted as an update notification.

[此处图片未下载成功]

. 4-11  Preset playback

.4.5. AWB result

AWB has been executed by the AW-HE50, the AWB result is posted as an update notification. The table below shows what is posted.

4-7

Remarks

ER3:OWS

execution successful AWB execution failed

below is the sequence which is followed when AWB is executed.

[AWB execution sequence]

“204 No Content” is returned as the response to the command, and when AWB is completed, “OWS” is

[此处图片未下载成功]

posted as an update notification.

details on what happens if AWB execution has failed, refer to “6. Error return”.

. 4-12  AWB result

. Camera information batch acquisihttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03tion

the information of the AW-HE50 can be acquired together as a batch.

[Command format] [Send]

://[IP Address]/live/camdata.html

:

Address&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;IP address of camera at connection destination

[Receive]

OK “Camera information”

:

information&#183;&#183;&#183;&#183;&#183;&#183;&#183;&#183;Camera information listed in Table 5.1;

[CR] and [LF] are used as the delimiters of the information.

[Sequence]

camera information is acquired from PC1. “200 OK [Camera information]” is returned as the response from the AW-HE50. Given below is the command sequence.

[此处图片未下载成功]

.5.1  Camera information batch acquisition sequence

5.1://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03information

/OFF status Model Name

p[data] OID:[data]

[data] section

: PowerOFF 1: PowerON AW-HE50 (fixed)

: 720/59.94p

: 720/50p 04: 1080/59.94i 05: 1080/50i 0B: 480/59.94i 0D: 576/50i Camera Title

:[data]

. 20 half-size characters

Camera information

[data] section

: Auto

: 0dB 14: 12dB 0B: 3dB 17: 15dB 0E: 6dB 1A: 18dB 11: 9dB 3C:  10 1B: –1

:  9 18: –2 36:  8 15: –3 33:  7 12: –4 30:  6 0F: –5 2D:  5 0C: –6 2A:  4 09: –7 27:  3 06: –8 24:  2 03: –9 21:  1 00: –10 1E: 0 AWB Mode Shutter Mode

:[data] OSH:0x[data]

: ATW

: AWB A

: AWB B

: OFF

: Step - 1/100 (N models)   1/120 (E/MC models) 5: Step - 1/250 6: Step - 1/500 7: Step - 1/1000 8: Step - 1/2000 9: Step - 1/4000 A: Step - 1/10000 B: SynchroScan

: OFF

: Low 2:http://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 High 0: 1: Manual2 2: Manual3 3: FullAuto 0: Camera

: ColorBar Speed With Zoom Pos. Preset Mode

[data] OSE:71:[data]

: OFF 1: ON 0: Mode A 1: Mode B 2: Mode C 0 : Desktop 1 : Hanging 0: OFF 1: ON 0: Manual 1: Auto

Position OSD ON/OFF Focus Mode

[data] OUS:[data] d1[data]

Camera information

Mode

Call Preset No. Total Detail Level ND Filter Option SW

d3[data] s[data] OSA:30:[data] d2[data] d6[data]

: Manual 1: Auto 1 to 100 0 (fixed) 0 (fixed) 0: OFF 1: ON

[data] section

(fixed) Iris Follow

:4F:[data]

: Close

…

: Open 0: No Error 1: Error 1 (fixed) 555: Wide …

: Tele 00: No Error 01: Error01 …

A: Error10 …

: Error30 555: Near …

: Far

to FFFFFFFFFF (40bit)  bit01 : Preset-No.001  …

: Preset-No.040

: Nohttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03 Entry 1: Entry

to FFFFFFFFFF (40bit)  bit01 : Preset-No.041  …

: Preset-No.080

: No Entry 1: Entry

Notice P/T Mode of Preset Zoom Position

:[data] rt[data] axz[data]

Status Info. rER[data]

Position axf[data]

Entry No.001 to 040 pE00[data]

Entry No.041 to 080

[data]

Camera information

Entry No.081 to 100

pE02[data]

[data] section

to FFFFFFFFFF (40bit)  bit01 : Preset-No.081  …

: Preset-No.100  bit21 : 0 (fixed)  …

: 0 (fixed)

: No Entry 1: Entry 000: Fast 250: Slow …

: Fast 0: Release  1: Set 0: Release  1: Set 0: Release  1: Set 0: Release  1: Set

Speed

[data]

-Up Limitation Set Tilt-Down Limitation Set Pan-Left Limitation Set Pan-Right Limitation Set

[dathttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03a] lC2[data] lC3[data] lC4[data]

. Error return

three errors ER1, ER2 and ER3 below are returned in response to control or query commands by the AW-HE50.

① ER1 (unsupported command)

error is generated when a command which is not supported by the AW-HE50 has been received by the AW-HE50.

: When the non-existent “XF” command is executed for the AW-HE50

[此处图片未下载成功]

. 6-1  Error (ER1)

② ER2 (busy status)

error is generated while AWB is being executed or at other times when the AW-HE50 is in the busy status.

: When the scene file is changed to “Manual1” while AWB is being executed

[此处图片未下载成功]

. 6-2  Error (ER2)

③ ER3 (outside acceptable range)

error is generated when the data value of a command is outside the acceptable rahttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03nge.

: When a data value of “90” for the “OGU (gain setting)” command whose data value is “08, 0B,

E, 11, 14, 17, 1A or 80” has been executed

[此处图片未下载成功]

Fig. 6-3  Error (ER3)

&lt;Appendix&gt;

in the example given below, this manual describes the HTTP messages using the URL format which complies with HTTP 1.0.

other words, communication is performed as in the [Send] and [Receive] sections below using the communication-based command format for camera and pan/tilt head control. (Example: http://192.168.0.10/cgi-bin/aw_ptz?cmd=#PTS5050&amp;res=1)

[Send]

command such as the ones listed below is sent after connection has been made to the specified port (default: 80) which has been set for the AW-HE50.

: GET

/cgi-bin/aw_ptz?cmd=#PTS5050&amp;res=1 HTTP/1.0[CR][LF] Request Request Method: GET [CR][Lhttp://www.wendangwang.com/doc/1ec1a278a3ad269232a40e03F]

URI: /cgi-bin/aw_ptz?cmd=#PTS5050&amp;res=1[CR][LF] Request Version: HTTP/1.0[CR][LF] HOST: 192.168.000.010[CR][LF]

[CR][LF] Blank line

[Receive]

message with the command name and result value contained in the message body of the HTTP response message is received.

this manual, this message is given as 200 OK “pTS5050”, but in actual fact commands such as the following ones are received.

/1.0 200 OK[CR][LF] Response Status: 200[CR][LF]

: Mon, 23 Aug 2010 00:00:00 GMT[CR][LF] Server: ver2.4 rev0[CR][LF] Connection: Close[CR][LF] Content-Type: Text/plain[CR][LF] Set-Cookie: Session=0[CR][LF] Accept-Ranges: bytes[CR][LF] Cache-control: no-cache[CR][LF] Content-length: 7[CR][LF] [CR][LF] pTS5050

※Size of message body Blank line Message body Header

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 https://www.wendangwang.com/

亿万文档资料，等你来发现