AR-B9680(RS02,RS03)

Pentium LGA775 High Performance 3D Gaming Embedded Motherboard

Edition: 1.0

Book Number: AR-B9680-06.05.02

@Copyright 2005

All Rights Reserved.

Manual first edition Apr 11, 2006

The information in this document is subject to change without prior notice in order to improve reliability, design and function and does not represent a commitment on the part of the manufacturer.

In no event will the manufacturer be liable for direct, indirect, special, incidental, or consequential damages arising out of the use or inability to use the product or documentation, even if advised of the possibility of such damages.

This document contains proprietary information protected by copyright. All rights are reserved. No part of this manual may be reproduced by any mechanical, electronic, or other means in any form without prior written permission of the manufacturer.

Trademarks

The Board is registered trademarks X-Fire Acrosser, IBM PC is a registered trademark of International Business Machines Corporation. Pentium is a registered trademark of Intel Technologies, Inc. Award is registered trademarks of Award Software International, Inc. Other product names mentioned herein are used for identification purposes only and may be trademarks and/or registered trademarks of their respective companies.

# Contents

Contents	3

Introduction	5

1.1 	Specifications:	5

1.2 What You Have	6

Installation	7

2.1 System Board Layout	7

2.2 Jumper & Header DESCRIPTION	9

Connection(AR-B9680)	11

Connection(AR-RS03)	11

CON1,2 : ISA Pin Header	12

Award BIOS Setup	13

4.1 Introduction	13

4.2 Starting Setup	13

4.3 Using Setup	14

4.4 Main Menu	15

4.5 Advanced BIOS Features	18

4.6 PnP/PCI Configuration Setup	20

4.7 Peripheral	21

4.8 PC Health	23

4.9 Boot	24

4.10 Exit Selecting	25

1

# Introduction

## 1.1 	Specifications:

CPU : Intel LGA775 CPU.

Chipset : Intel 945G and ICH7.

RAM memory :  Two DDR2 DIMM Socket support to 2GB.

Display Controller : Intel 945G Supports non-interlaced CRT monitors.

IDE Interface : One 44pin 2.0mm IDE channel.

Compact Flash TM interface : Supports Two Compact Flash TM Type II  socket for Compact Flash Disk Share with IDE.

Series ports : Two high-speed 16C550 compatible UART ports.

USB port : Support Eight USB 2.0 compatible ports.

Audio Connector :  Supports Line-in, Line-out, MIC-in.

PS/2 Mouse/Keyboard Connector

Watchdog timer : Time setting form 1  to 255 second / minute  System Reset generate when CPU did not periodically trigger the timer.

REALTEK LAN Controller : 2 ports REARTEK 8100C 10/100BASE-TX. Connected to your LAN through RJ45 connector.

Dimension : 310mm(W) X 200mm(L).

Operating Temperature : -10 ~ 55 C ( CPU needs Cooler ).

## 1.2 What You Have

In addition to this User's Manual, the board package includes the following items:

PCIE Riser Card (AR-RS02)

PCI Riser Card (AR-RS03)

System board (AR-B9680)

User’s Manual

Drive CD

2

# Installation

This chapter describes how to install system. At first, the layout of board is shown, and the unpacking information that you should be careful is described.  The jumpers and switches setting for the board configuration.

## 2.1 System Board Layout

## 2.2 Jumper & Header DESCRIPTION

CCMOS1 : CMOS reset pin header.

Default setting : 1-2 short

| CCMOS1 | DESCRIPTION |
| --- | --- |
| 1-2 | Normal Operation |
| 2-3 | Reset CMOS |

JP7(for CON1) & JP8(for CON2) : Select CF Master/Slave mode.

Default setting : JP7 open, JP8 open

| JP7,8 | DESCRIPTION |
| --- | --- |
| Short | Master |
| Open | Slave |

FPIO2 : HDD LED, Reset, PSON Connector.

| PIN | DESCRIPTION | PIN | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | HDD LED+ | 2 | REV |
| 3 | HDD LED- | 4 | REV |
| 5 | RESET-(GND) | 6 | PSON- (GND) |
| 7 | RESET+ | 8 | PSON+ |
| 9 | NC | 10 | NC |

FPUSB1 :  USB4, 5 Connector.

| PIN | DESCRIPTION | PIN | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | VCC | 2 | VCC |
| 3 | DATA-(port4, 6) | 4 | DATA-(port5, 7) |
| 5 | DATA+(port4, 6) | 6 | DATA+(port5, 7) |
| 7 | GND | 8 | GND |
| 9 | NC | 10 | NC |

FAN1, 2, SYSFAN:  Fan Connector.

| PIN | DESCRIPTION |
| --- | --- |
| 1 | GND |
| 2 | FAN+ (12V) |
| 3 | FANSP |

CPUFAN:  Fan Connector.

| PIN | DESCRIPTION |
| --- | --- |
| 1 | GND |
| 2 | FAN+ (12V) |
| 3 | FANSP |
| 4 | Control |

3

# Connection(AR-B9680)

COM2 : RS-232 Serial port (2.0mmPin Header).

| PIN | DESCRIPTION | PIN | DESCRIPTION |
| --- | --- | --- | --- |
| 1 | DCD | 2 | RX |
| 3 | TX | 4 | DTR |
| 5 | GND | 6 | DSR |
| 7 | RTS | 8 | CTS |
| 9 | RI | 10 | NC |

Mouse, Keyboard, COM1, VGA, Line Out/In, Mic, Lan, USB Connector.

MIC       LAN2       LAN1

MOUSE                                                                    LINE IN     USB2      USB0

KEYBOARD    COM1                     VGA                  LINE OUT   USB3      USB1

# Connection(AR-RS03)

## CON1,2 : ISA Pin Header(Not fully the ISA function, only gives the ODM customer use.)

4

# Award BIOS Setup

## 4.1 Introduction

This chapter discusses the Setup program built into the BIOS.  The Setup program allows users to configure the system.  This configuration is then stored in battery-backed CMOS RAM so that it retains the Setup information while the power is off.

## 4.2 Starting Setup

The BIOS is immediately active when you turn on the computer. While the BIOS is in control, the Setup program can be activated in one of two ways:

- By pressing <Del> immediately after switching the system on, or

- By pressing the <Del> key when the following message appears briefly at the bottom of the screen during the POST (Power On Self-Test).

Press DEL to enter SETUP.

If the message disappears before you respond and you still wish to enter Setup, restart the system to try again by turning it OFF then ON or pressing the "RESET" button on the system case.  You may also restart by simultaneously pressing <Ctrl>, <Alt>, and <Delete> keys.  If you do not press the keys at the correct time and the system does not boot, an error message will be displayed and you will again be asked to...

PRESS F1 TO CONTINUE,  DEL TO ENTER SETUP

## 4.3 Using Setup

In general, you can use the arrow keys to highlight items, press <Enter> to select, use the PageUp and PageDown keys to change entries, press <F1> for help and press <Esc> to quit.  The following table provides more details about how to navigate in the Setup program using the keyboard.

| Key | Function |
| --- | --- |
| Up Arrow | Move to the previous item |
| Down Arrow | Move to the next item |
| Left Arrow | Move to the item on the left (menu bar) |
| Right Arrow | Move to the item on the right (menu bar) |
| Esc | Main Menu: Quit without saving changes Submenus: Exit Current page to the next higher level menu |
| Move Enter | Move to the item you desired |
| PgUp key | Increase the numeric value or make changes |
| PgDn key | Decrease the numeric value or make changes |
| + key | Increase the numeric value or make changes |
| - key | Decrease the numeric value or make changes |
| Esc key | Exit Menu -- Quit and not save changes into CMOS Status Page Setup Menu and Option Page Setup Menu -- Exit current page and return to Main Menu |
| F1 key | General help on Setup navigation keys |
| F5 key | Load previous values from CMOS |
| F6 key | Load the fail-safe defaults from BIOS default table |
| F7 key | Load the optimized defaults |
| F10 key | Save all the CMOS changes and exit |

## 4.4 Main Menu

The items in Standard CMOS Setup Menu are divided into 10 categories.  Each category includes no, one or more than one setup items.  Use the arrow keys to highlight the item and then use the <PgUp> or <PgDn> keys to select the value you want in each item.

Figure 1:  The Main Menu

Main Menu Selections

| Item | Options | DESCRIPTION |
| --- | --- | --- |
| Date | MM DD YYYY | Set the system date. |
| Time | HH : MM : SS | Set the system time |
| IDE Primary Master | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Primary Slave | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Secondary Master | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| IDE Secondary Slave | Options are in its sub menu (described in Table 3) | Press <Enter> to enter the sub menu of detailed options |
| Drive A & Drive B | None 360K, 5.25 in 1.2M, 5.25 in 1.720K, 3.5 in 1.44K, 3.5 in 2.88K, 3.5 in | Select what kind of floppy type you install |
| Video | EGA / VGA CGA 40 CGA 80 Mono | Select what type of Display you use |
| Halt On | All Errors No Errors All, but Keyboard All, but Diskette All, but Disk/Key | Select the situation in which you want the BIOS to stop the POST process and notify you |
| Base Memory | N/A | Displays the amount of conventional memory detected during boot up |
| Extended Memory | N/A | Displays the amount of extended memory detected during boot up |
| Total Memory | N/A | Displays the total memory available in the system |

Table 1 Main Menu Selections

#### IDE Adapters

The IDE adapters control the hard disk drive.  Use a separate sub menu to configure each hard disk drive.

Figure 2 shows the IDE primary master sub menu.

IDE HDD Auto-Detection	[Press Enter]

IDE Primary Master		[Auto]

Access Mode [Auto]

Capacity					0MB

Cylinder					0

Head					0

Precomp					0

Landing Zone				0

Sector					0

Figure 2  IDE Primary Master sub menu

Use the legend keys to navigate through this menu and exit to the main menu.  Use Table 2 to configure the hard disk.

| Item | Options | DESCRIPTION |
| --- | --- | --- |
| IDE HDD Auto-detection | Press Enter | Press Enter to auto-detect the HDD on this channel. If detection is successful, it fills the remaining fields on this menu. |
| IDE Primary Master | None Auto Manual | Selecting ‘manual’ lets you set the remaining fields on this screen. Selects the type of fixed disk. "User Type" will let you select the number of cylinders, heads, etc. Note: PRECOMP=65535 means NONE ! |
| Capacity | Auto Display your disk drive size | Disk drive capacity (Approximated). Note that this size is usually slightly greater than the size of a formatted disk given by a disk checking program. |
| Access Mode | CHS LBA Large Auto | Choose the access mode for this hard disk |

Table 2 Hard disk selections

## 4.5 Advanced BIOS Features

This section allows you to configure your system for basic operation.

Figure 3  Advanced menu

APIC Mode

This item allows use Advanced Programmable Interrupt Controller feature. The Choice: Enabled, Disabled.

#### Quick Power On Self Test

This category speeds up Power On Self Test (POST) after you power up the computer.  If it is set to Enable, BIOS will shorten or skip some check items during POST.

| Enabled | Enable quick POST |
| --- | --- |
| Disabled | Normal POST |

Full Screen LOGO Show

This item allows you to enable or disable show full screen LOGO.

The Choice: Enabled, Disabled.

USB Keyboard Support

This item allows you to enable or disable USB keyboard support.

The Choice: Enabled, Disabled.

PS/2 Mouse Function

Disabled-prevents any installed PS/2 mouse from functioning but frees up IRQ12.Enabled-allows the operating system to determine whether to enable or disable the mouse. Choice: Enabled, Disabled.

Init Display First

This item allows you to choose which Display to be first detected.

The Choice: PCI Slot, On Board / AGP.

Intel VGA Share Memory

This item allows you to Choose the Frame Buffer size for Display.

The Choice: 1MB, 4MB, 8MB, 16MB, 32MB.

Boot Display

This item allows you to choose display interface.

The Choice: Vbios default, CRT, EFP, TV, CRT + EFP, CRT + TV.

Panel Type

This item allows you to choose display panel type and resolution.

The Choice: 640x480,800x600,1024x768.

ACPI Function

This item allows you to enable or disable Advanced Configuration and Power Management (ACPI) function.

The Choice: Enabled, Disabled.

ACPI Suspend Type

This item allows you to Choose Suspend Type for ACPI function.

The Choice: S1(Pos), S3(STR), S1 & S3.

Power Supply Type

This item allows you to choose the Type of Power Supply in use.

The Choice: AT, ATX.

PWRON After Power-Fail

This item allows you to choose the Option of  Power Status after Power Fail by ATX Power Supply.

The Choice: Former-STS, On, Off.

## 4.6 PnP/PCI Configuration Setup

Figure 4  PnP/PCI menu

#### Resource controlled by

The Award Plug and Play BIOS has the capacity to automatically configure all of the boot and Plug and Play compatible devices.  However, this capability means absolutely nothing unless you are using a Plug and Play operating system such as Windows(95.  If you set this field to “manual” choose specific resources by going into each of the sub menu that follows this field (a sub menu is preceded by a “(”).

The choice: Auto(ESCD), Manual.

#### IRQ Resources

When resources are controlled manually, assign each system interrupt a type, depending on the type of device using the interrupt.

#### IRQ3/4/5/7/9/10/11/12/14/15 assigned to

This item allows you to determine the IRQ assigned to the ISA bus and is not available to any PCI slot. Legacy ISA for devices compliant with the original PC AT bus specification, PCI/ISA PnP for devices compliant with the Plug and Play standard whether designed for PCI or ISA bus architecture.

The Choice: PCI Device, Reserved.

## 4.7 Peripheral

Figure 5  Peripheral menu

#### Onboard Serial Port 1/Port 2

Select an address and corresponding interrupt for the first and second serial ports.

The choice: 3F8/IRQ4, 2E8/IRQ3, 3E8/IRQ4, 2F8/IRQ3, Disabled,                    Auto

#### UART Mode Select

Select  the Function Mode for UART.

The choice: IrDA, ASKIR, Normal

#### Onboard Serial Port 3/Port 4

Select an address and corresponding interrupt for the first and second serial ports.

The COM3 choice: 3F8/IRQ11, 2E8/IRQ11, 3E8/IRQ11, 2F8/IRQ11, Disabled

The COM4 choice: 3F8/IRQ10, 2E8/IRQ10, 3E8/IRQ10, 2F8/IRQ10, Disabled

#### Onboard Parallel Port

Select 3BC/IRQ7 to enable On Board Parallel Port as first Parallel Interface.

The choice: Disable, 378/IRQ7, 278/IRQ5, 3BC/IRQ7.

#### USB Controller

Select Enabled if your system contains a Universal Serial Bus (USB) controller and you have USB peripherals.

The Choice: Enabled, Disabled.

#### USB 2.0 Controller

This Entry is for disable / enable EHCI controller only. The Bios itself may / may not have high speed USB support. If the Bios has high speed USB support built in, the support will be automatically  turn on when high speed device were attached.

The Choice: Enabled, Disabled.

AC97 AUDIO

The Choice: Auto, Disabled.

## 4.8 PC Health

Figure 6  H/W Monitor menu

Shutdown Temperature

This item allows the system to reset when temperature reach the trigger level.

The Choice: Disabled, 60°C/140°F, 65°C/149°F, 70°C/158°F, 75°C/167°F

## 4.9 Boot

Figure 7  Boot menu

#### First/Second/Third/Other Boot Device

The BIOS attempts to load the operating system from the devices in the sequence selected in these items.

The Choice:

- Floppy		……….	[ ]

- LS120		……….	[ ]

- Hard Disk  ….	[ ]

- CDROM		…	…….[ ]

- ZIP100   		……….	[ ]

- USB-FDD		 ..	…...[ ]

- USB-ZIP   ..	…...[ ]

- USB-CDROM	  ..	[▪]

- On Board LAN	…[ ]

- Disabled		…..	……[ ]

## 4.10 Exit Selecting

Figure 8  Exit menu

- Save & Exit Setup

- Load Optimized Defaults

- Exit Without Saving

- Load Fail-Save Default

### Save  & Exit Setup

Pressing <Enter> on this item asks for confirmation:

Save to CMOS and EXIT (Y/N)?  Y

Pressing “Y” stores the selections made in the menus in CMOS – a special section of memory that stays on after you turn your system off.  The next time you boot your computer, the BIOS configures your system according to the Setup selections stored in CMOS. After saving the values the system is restarted again.

### Load Optimized Defaults

### Use this menu to load the BIOS default values that are factory settings for optimal performance system operations.  While Award has designed the custom BIOS to maximize performance, the factory has the right to change these defaults to meet their needs.

When you press <Enter> on this item you get a confirmation dialog box with a message similar to:

Load Optimized Defaults (Y/N) ?  N

Pressing ‘Y’ loads the default values that are factory settings for optimal performance system operations.

### Exit Without Saving

Pressing <Enter> on this item asks for confirmation:

Quit without saving (Y/N)?  Y

This allows you to exit Setup without storing in CMOS any change.  The previous selections remain in effect.  This exits the Setup utility and restarts your computer.

### Load Fail-Safe Defaults

### Use this menu to load the BIOS default values that are factory settings for safety system operations.

When you press <Enter> on this item you get a confirmation dialog box with a message similar to:

Load Fail-Safe Defaults (Y/N) ?  N

Pressing ‘Y’ loads the default values that are factory settings for Fail-Safe system operations.

# Text boxes

A62