1	XEEDER Hotel Lock System networked Overview	3

2	Component	4

2.1	Connection	4

2.2 Equipment Required	5

3	Setting Up	7

3.1	Install Hotel Lock System networked	7

3.2	Install Xentral v1.0 server	8

4	Interface	10

4.1	Main Window	10

4.2	Menu	11

4.3	Shortcut	12

4.4	Icon	13

4.5	Filter	13

4.6	Track Record	14

4.7	 Right-click mouse menu	14

5	Initialization	15

5.1	Register	15

5.2	Default setting	15

5.3	Building Rooms	17

5.4	Add operators	22

5.5	Explanation of Status sign	23

6	Issue Card	24

6.1	Time card	24

6.2	Setting Card(Adjust time)	24

6.3	Check-out card	24

6.4	Loss-Report card	25

6.5	Guest card	26

6.6	Stay Extend.	27

6.7	Check-out	27

6.8	Verify/Revoke	29

6.9	 Card Search	29

6.10	Mater card/ Area card/Building card/Floor card/Passage card/Emergency card	30

6.11	Override function	32

7	Lock Events	33

7.1	Real time Supervising	33

7.2	Failed Issued	33

7.3	Guest Search/Room Search	33

7.4	Lock Events	34

8	Advanced skills	36

8.1	System operating parameters and settings	36

8.2	Configuration file instruction(ILocksoft.ini )	37

# XEEDER Hotel Lock System networked Overview

Xeeder Hotel lock system Networked is a new product that developed especially for the high security building management. Adopted TCP/IP protocol and UTP CAT-5 cable connection, powered by POE, all locks and computers (server and client) are in a LAN, computers can monitor and control all locks status and remote unlock all locks; Locks save all records of reading card and unlocking, these records can be collected by computers at any moment. Some cards’ functions are replaced by computer operation, to some extent, it may help to reduces cost, but it is more efficient and safer.

.

Features ：

    - Real time monitoring all rooms，collecting lock events and the type of  unlocking card by computer at any moment.

    - Powered by POE(Power over ethernet) power adapter and internal battery, auto switch when external power supply stops .

    - Center control to open the door, remote unlock and card unlock, show the records in computer simultaneously.

    - Multi users with different rights ,  5,000 users + 10,000 events per lock, flash saves events, can achieve  multi-card to a door and  multi-door in a card.

    - In case of emergency, control all locks in unlocking or locking status through computer.

    - Guest records and Card issued records search and print able

    - Based on TCP/IP technology but no limit to quantity in one LAN (project).

    - Free combination of rooms/time table in 1 card, Passage mode for meeting case.

Over current protection, Low Battery Voltage warning(beep and red light).

This is not only a software suit for hotels but also useful to office, apartment, school and government.

# Component

## Connection

## 2.2 Equipment Required

|  | Name | function |
| --- | --- | --- |
|  | At least 1pc personal computer with Microsoft XP/Vista OS | The main hardware for install software and connect encoder CPU: Pentium II or above、64M above RAM Os: Microsoft Windows 2K/2K3/XP/VISTA Pentium 150MHz or higher processor 200MB Hard Drive Space or more CD-ROM Drive Mouse and Keyboard USB port 1.1/2.0 Soft size: 10.0MB |
|  | Mifare-1k Classic RFID card | Key card, holder have each piece. MF 1K S50 |
|  | Mifare-1(M1) card encoder | Data card, It is used for retrieving open records from the lock. E1208-M1 |
|  | POE power adapter | Supply power to lock from AC 100-240V and gives data transfer channel between computer and locks. |
|  | Switch or Hub | Connect all locks with computer, build up a LAN 10/100M Standard Ethernet Switch |
|  | UTP(Unshielded Twisted Pair) CAT-5 cable | Connect and focus all lock together in a LAN(Local Area net) and connect to PC |
|  | Door loop | Steel Protect cable go through the door and the door frame, and protect the cable from impact and bend outside |
|  | Networked lock | Networked lock support the all functions |

# Setting Up

## Install Hotel Lock System networked. Every computer used issuing card needs to installed

Step1: Put Xeeder CD into computer’s CD-ROM，open my computer and double click DVD drive.

Step2: double click the icon  ,so enter the main guide.

Step3: choose the second one install hotel lock system to set up immediately.

Step4: Click next to continue, choose your suitable path

## Install Xentral v1.0 server

Xentral is a small tool that supply communication channel between PC and lock. It is installed in a same computer with Hotel lock system networked if your hotel use only one computer to issue card. However, if you have more than one computer to issue card, Xentral has to be installed in an appointed computer used as server, and Hotel lock system networked is installed in each other computer used as client (issuing card computer).

Step1: In main Guide, click the last one Networked version

Step2:click next to continue, choose your suitable path

# Interface

## Main Window

Double click the software shortcut icon on your computer desktop , startup network lock system. Then, choose user system and enter password 0, you will come into the main window immediately.

The main window as the following:

The system has not been registered, so its top shows DEMO.

## Menu

System Setting-

Room Setting-

Operator-

Maintain-

Issue Card-

Help-

## Shortcut

## Icon

Empty house-Room is ready to check in. [Status-OK]

Lock-The room is locked and stops to be used for some reasons. [Status-Bad]

Passport-This room has been booked by guest. [Status-Booked]

Calendar-Hotel leaves the room self-use. [Status-Self-use]

Coffee-The room is dirty. [Status-Dirty]

Person-The room has been checked in by guest. [Status-Busy]

## Filter

## Track Record

Occupied- Quantity of busy rooms

Self-use- Quantity of rooms leaved for self-use

Booked- Quantity of rooms booked by guests

Dirty- Quantity of dirty rooms

Bad- Quantity of repairing rooms

Total- Quantity of all rooms in hotel

This is used for showing the unlocking events, when card, key and computer open the door, it is showed here instantly.

## Right-click mouse menu

# Initialization

After complete installation of software, you should do initialization work to make all lock connecting well with computer, otherwise you could not start enjoy the functions of networked.

## Register

Step1: System Setting->Register                                               Click OK

Step2: Place the authorized card on the encoder                       Click OK and enter licence code

Step3: Click Update, register successfully. Restart software to use.

## Default setting

System Setting->System Parameter

General:

Advanced:

Status color:

Networking setting:

All the items you have finished, click apply to go into effect.

## Building Rooms

Step1: Room Setting->Room Type Setting

You can rename, define rate and quantity allowed to live in, you can add more new room type, click save and close it.

Step2: Room Setting->Build Setting

You can rename all the building and add new. When you finished , save and close it.

Step3: Room Setting->Room Details

TCP/IP setting:

Finish this, continue to set next room. If you use consecutive IP, you can click Auto add. In the end, Set all IP and restart the software..

Note:

1. In order to avoid IP repetition, we suggested you add particular IP for your computer as possible as you can ( such as 192.1.1.1) . Because if your IP is same as others’, it will be unavailable. If your hotel has more rooms and one IP is not enough, you could add more new IP. E.g. My computer’s real IP is 192.168.0.136, this is a usual IP, however, avoiding duplication with others, I add a new IP to my computer 192.168.1.1, and all locks’ IP should follow with 192.168.1.X.

2. When MAC reach ‘A’ ,  you must change into 0, because data in program is hex, but we use decimal.  e.g. if current MAC is A0000248, auto add, then reach 249 and the next is 24A, we should change into 250, then auto add again

3. When your setting is finished, click Set all IP, this is to validate if all locks connect to your computer, at the same time, locks will continuously beep if succeed. If you have to change lock into another, when you finish changing new lock, click change lock is ok. Once you modify MAC, you should do that.

4. In order to start up quickly and reduce errors, Once you set IP again or modify other configurations , we suggest you restart Lock System Software.

Step4:  Room Setting->Common door Setting

TCP/IP message:

Step3: Room Setting->Default common doors

a. Use default common doors

You should do nothing for use default common doors because each time when you issue a new guest card you will find the Auto common doors already been selected, That’s the common doors you chose in step select default common doors

b. select a un-default common doors.

You can adjust common doors for a guest who has a special request.

Cancel the selection of ‘Auto common doors’ you will find the big button of ‘Common doors…’become press able.

## Add operators

Hotel usually has some different operators with different rights such as supervisor, manager and receptionist. To make your management easier, first you have to add new operator’s name, level rights, initial password.

1.Operator->Entitle Operators

Step1: Edit system operator. Modify system operator information, Grade and operator can not be changed. System operator is the highest grade.

Step2: Add new operator. Click Add and edit information. Save it.

2. Switch operator. Finish adding, different operator enter software system has different right with different password. E.G.  Susan.

Step1: Log in

Step2: Look over the window. Because Susan is a receptionist, some operation is limited, such as initialization, building rooms, issuing functions ect.

At bottom of window, current operator is showed.

Also you can switch operator directly. Operator->Switch operator

3 .Modify password.

Operators may modify their passwords, Operator-> Modify password

## Explanation of Status sign

1. Icon status

Lock is connected to computer successfully.

Lock to computer connection failed.

Door is been opened by computer.

There has been one guest checked in this room. If the room is double room, you have issued 2 cards for two guests, ×1 will change into ×2, that is quantity of cards.

This room type is standard double room, the short name you defined before is showed at bottom。

# Issue Card

## Time card

Time card is just used in un-networked lock system to activate time of lock. In networked system, it is valueless, please don’t use.

## Setting Card(Adjust time)

In Xeeder Hotel Networked Lock System, this is just used to adjust lock’s time when lock power source supply(both external power and battery) is off in a certain period, because time has lost, if don’t do this, there will be errors. But don’t issue any card. Maintain ->Setting card.

## Check-out card

Check-out card is issued for guests when they want to leave hotel to check out. Maintain->Check-out card, or directly switch in time card issued form.

## Loss-Report card

Hotel should offer safe room for guest. The card lost usually happens everyday. Make the lost card unable work is necessary and very important. You should Issue ‘Loss report’ card and read it on lock. Maintain->loss report

## Guest card

Issue card->Guest card

Note: Auto common door is common door set before, if you want to change, cancel it, select from list.

Step3: Place card to encoder.

## Stay Extend.

Sometimes guests want to stay longer than the period in issued card, you should make the card staying extend.

Step1: Ask how many days extending and get the card from guest.

Step2: Place card onto encoder

Step3: Issue card->Check-out

## Check-out

1.Check-out with card.

Step1: Get the card submitted by guest and place it onto encoder.

Step2: Issue card->Check out or click shortcut

Step3: Click Card+Room

2.Check-out (without need cards)

Step1: Find rooms by guest name or check in record

Step2: Select room icon and right click, click Check-out.

Note: Checking out without card requires to make the card unable to work any longer.

To make the previous card not working anymore on lock, there has 2 ways.

1 .Use Override function.

Issue a new card by selecting ‘Override’.  After the new guest read this card on  lock(e.g. 101), the previous 101card will not unlock anymore by red light.

2. Read the loss report card,(This is especially for the lost card)

## Verify/Revoke

Sometimes you need to revoke card to clear card content, in order to write new information. Before revoking, to reduce mistake you should examine what the content is by using Verify function.

Step1: Place the card to encoder, Issue card->Verify/Revoke, or click shortcut

Step2: click Revoke card

Status is OK.

Note: Be cautious to use Revoke, once card is revoked, you can’t recover any more.

## Card Search

Issue Card->Card search

## Mater card/ Area card/Building card/Floor card/Passage card/Emergency card

All these cards can be issued in one multi-form.

1. Master card

This kind of card can open all locks in a certain period, including in inside locking status.

Issue Card-> Master Card

2. Area card

It can open certain area’s doors in certain period.  Max 4 random areas in one card (area should be defined when building rooms),It cannot open the doors when thumb-turn is used.

Switch to Area card.

3. Building card

It can open a certain building’s doors in certain period. It can not open the doors when thumb-turn is used.

4. Floor card

It can open certain floor’s doors in certain period. It cannot open the doors when thumb-turn is      used

5. Passage card

This card can make all doors into unlocking status which allow lock without card in certain period, including inside locking status.

6. Emergency card

This kind of card can open all lock in certain period; even if thumb-turn is used.

## Override function

In case lost card usually happens in your hotel, every time issue card please select ‘Override’

How it works?    The key is card’s issued date is different between the early and the new.

Software will make a note in new card from the time new issued by selecting Override

For example, room 101 card was taken away by the guest used to living in 101. Today (e.g.Jul.20.11:00) there is a new guest need to live in 101, when issue card for him, select ‘Override’.

When the new guest read this card on the door, the lock give up working for all guest cards which issued early than Nov03 11:00.The previous 101 card can not unlock anymore.

# Lock Events

## Real time Supervising

If any door is opened by any card, key or lock read any invalid car placed maliciously, the records       is showing in a form on computer immediately.

## Failed Issued

This is used to look over the failed information when issue cards.

Maintain->Failed Issued.

## Guest Search/Room Search

1. Maintain->Guest Research. You can see all the information of guests who have checked in.

2. Maintain -> Room Search. It is same function as Room List in Check-in, In order to search room quickly, we usually use the Filter.

## Lock Events

Xeeder Networked Lock can memorize all unlocking events both using key and card (as more as 5000 events). Any time, you can collect locking events from lock to your server so that search records can be searched by choosing time period according with you.  This is quite convenient for your management.

Step1: Select a certain room (can be several rooms one time), then right-click, choose Lock Events.

Step2: click OK to enter the event form, select Including History to collect all events. Then collect in sequence by room NO. and date.

Step3: After finishing collecting, you also may search events what is useful to you from above. Fill in the period in Read card from or cancel some rooms then click search.

Note: If remote unlocked by computer, card type is blank and card No. is zero or blank. If collect more than one room at one time, records is collected according to room No. firstly, according to the time secondly in one room. You can clear data, collect again.

Records can be saved as Excel file and printable. But only searched events is visible in print status, collected events is un-visible. In other word, if you want to print records, please search from local sever in advance after collecting.

# Advanced skills

## System operating parameters and settings

1. The time that control motor clockwise rotation and anti-clockwise rotation is always 200ms.

Time of motor Interval of clockwise rotation and anti-clockwise is 1 to 25 sec. 6 sec default can be changed.

Motor clockwise rotation shows unlocking, beep tone is Do, Re, Mi, and blue lights. Motor anti-clockwise shows that can not open the door, beep tone is Mi, Re, Do, and blue light out.

2. Opening by keycard.

Blue light, lock the door again after delaying 6 sec (can be changed). If detect the action to open the door (detect through switch tongue), lock the door immediately (motor rotates anti-clockwise) and save one record.

3. Opening by Machinery key

Blue light, one beep, release it after the status over.

4. Door is pretended to be locked.

2 sec later (can be changed between 1 to 25 sec), red light flashes every 3 sec , 10us one    time, release this after status is changed.

5. Detect door contact

Always detect status of door contact, send the status to PC when asking.

Hotel lock light flashing table:

| Read Card Reaction | Guest card Building card Area card Floor card | Master card | Passage card Emergency card | Loss-report card |
| --- | --- | --- | --- | --- |
|  | 1.The No.(room/building/area/floor)in card doesn’t coincide with the lock, can not open the door. 2..Card has been loss-reported, can not open the door. |
|  | Deadbolt override is started up, can not open the door. |
|  | 1. Card’s effective time is incorrect, maybe time of now is earlier or later. 2. Time in lock is error. |
|  | Read card successfully, open the door. |

## Configuration file instruction(ILocksoft.ini )

Path=Hotel lock system V5.6\ ILockSoft  , this is to help you modify some configuration

to add or cancel certain function.

| Name | Default | value range | Description | Function |
| --- | --- | --- | --- | --- |
| TimeTolerance | 0 | =0 | In minutes | Time warp compensation |
| LanguageID | 1033 | 1028,1032,1033,2052 | Chinese | The type of language showed |
|  |  | =1033 | English |  |
| *DataExtension | 0 | =1 |  | Use 3 data[48Byte],with common door |
|  |  | =0(or others) |  | Use 2 data[32Byte] |
| *RoomExtension | 0 | =1 |  | Guest card can open 8 doors |
|  |  | =0(or others) |  | Guest card can open 4 doors |
| *Lift | 0 | =1 |  | Use elevator |
|  |  | =0( or others ) |  | No elevator |
| *EncodeDirectly | 0 | =1 |  | Issue card directly without logging out |
|  |  | =0( or others ) |  | Must clear card’s content, then can issue card. |
| *MoreGuestCards | 0 | =1 |  | One room can be issued several guest cards |
|  |  | =0( or others ) |  | One room jus can be issued one card. |
| EnOpeningMusic | 0 | =1 |  | Open door with music |
|  |  | =0( or others ) |  | Open door without music |
| *EnNormalOpen | 0 | =1 | With passage mode | Guest card、Building card、Floor card、Area card passage mode option |
|  |  | =0 ( or others ) |  | Without passage mode |
| Softver | 50 | =50 | Version 5.0 | New version registration code |
|  |  | =46 | Version 4.6 | Old version registration code |
| LockEepType | $08 | =$08 | 800 unlock events collection | Lock eeprom capacity |
|  |  | =$02 | 200 unlock events collection |  |
| *DoorAlarmSound | $00 | =$00 | 3beeps and red light every 3 sec | Warning rings when door pretend to be locked |
|  |  | =$10 | Continuous alarm |  |
|  |  | =$20 | Red light without beep |  |
|  |  | =$30 | No alarm |  |
| *MotorInterval | $00 | =$00 | 0.2sec | Time of motor rotation |
|  |  | =$01 | 0.2sec |  |
|  |  | =$02 | 0.4sec |  |
|  |  | =$03 | 0.6sec |  |
|  |  | =$3F | 12.6sec |  |
| M1CommondataSector | $0e | =$0e |  | Sectors used in common information field such as elevator controller. |
| Server Ip | 127.0.0.1 |  |  | Sever IP |
| LocalServer | 1 | 0 | Local computer is not server | If local computer runs as server or not，if the server run at local computer or not. |
|  |  | 1 | Local computer is server |  |
| NetWorkLock | 0 | 0 | Not start up networked lock | If software start up networked lock function or not. |
|  |  | 1 | Start up networked lock |  |
| DoorDelayTime | 4 | 1-25s | Delay of unlocking the door | Delay of controller unlocking the door |
| Data saving mode in controller |  | 0 | Data is covered with new when full | Data retention mode in controller. |
|  |  | 1 | Alarm when full |  |
| HostilityBrushCard | 4 | 4-100 |  | Times of controller invalid credit card |
| OldIpAdress | 192.168.0.100 |  |  | Original IP |
| Subnetmask | 255.255.255.0 |  |  | Subnet mask |
| Gateway | 192.168.0.1 |  |  | Gateway |
| NetWorkSwitch | 0 | 0 | Not start networked switch |  |
|  |  | 1 | Start networked switch |  |
| CheckMCDevice | 0 | 0 | Network switch detects door contact. | Use door contact signal of networked switch. |
|  |  | 1 | Network lock detects door contact. | Use networked lock contact signal |
| CheckDoorState |  | 0 | Not detect door contact |  |
|  |  | 1 | Detect door contact |  |
| Checked in |  |  |  | Color of Checked in room interface. |
| Normal |  |  |  | Color of OK room interface. |
| Booked |  |  |  | Color of Booked room interface. |
| Reserved |  |  |  | Color of self-use room interface. |
| Dirty |  |  |  | Color of Dirty room interface. |
| Service |  |  |  | Color of Repairing room interface. |

# Text boxes

Choose a suitable path for you

System Parameter-Set Hotel name/ correlative default/ rooms status color/start or stop

some functions.

Register- Register the software system.

Licence code update-For limited user (the trial period has overdued) update the code to continue using.

Import Database- for multi-terminals in one hotel, they can import public database to share from here.

Language-Change the software’s language into a type you want.

Database Backup- Save database.

Database Recover-Recover database.

Exit- Exit the software.

Room type setting-For setting room types

Building setting-For seting building’s name

Room details-For building rooms with ID, floor, building, area ID, type status and TCP/IP setting.

Entitle Operators-Add new operator to system and set password.

Switch Operator-Change operator.

Modify Password-Change a new password.

Time card -issue time card to activate (modify) locks’ clock, but in networked lock system, it is valueless, please don’t use it.

Setting card-issue setting card to set doors (common doors) ID, but in networked lock system, this is just used as adjusting lock’s time when lock time has error.

Check out card- issue a Check out card to force check out a room.

Data Startup card- In networked lock system, it is valueless, please don’t use it.

Guest search-Search appointed guest who has checked in.

Room search- Search room which the guest wants to check in.

Lock events-Collect records that locks read card and open the door from the lock.

Guest card- Enter to issue Guest card, same effect as double click room icon or shortcut. Group Check in- Start group issuing cards from here.

Stay Extend- modify staying days longer for guest card.

Check out- Read guest card to check out.

Verify/Revoke- Check the card’s content or make the card empty.

Card search- Find a card that has been issued.

Master card- Issue Master card, Master card can open all rooms including deadbolt.

Area card- Issue Area card, it can open all rooms in a same area, but firstly your setting should be ok when build rooms.

Building card- Building card can open one whole building’s all rooms but not including deadbolt

Floor card- It can open all rooms at one floor but not including deadbolt.

Passage card- It can open all doors inluding deadbolt and after reading this card, the door becomes passage mode which means can open without card and key including deadbolt.

Emergency card- open all doors in emergency case including deadbolt.

Help-Open the help file.

About…-About Hotel Lock System.

Modify the staying days longer or shorter

Make check out for guest

Check the card’s content or revoke it empty

Change another operator

Exit Hotel Lock System

This filter is not only used for quickly searching room the guests want, but also can see all building and room’s types and status. When you ask guest what type room he wants to check in, then, pitch on them, rooms according with you will show on the right window.

Usage-

1. Select room type firstly because guest usually have an idea what rooms they want firstly.

(Default is All type).Then all rooms of the selected room type comes out (E.g. Standard rooms) .

2. Select room status, usually you should find an ‘OK’ room for the new come guest.

Click OK, here you will find all rooms of free Standard room

3. Building select required in case hotel has several different buildings.

You can enter different floor by click the ‘+’ besides the building 1.

‘+’means there has ower-level directories in it.

Here in building 1 there are many floors (at least 1 floor exist)

Name- Enter your hotel name

Due check out time- your hotel’s rule of check out time

Default staying days-a default days that when issue card window opened.

Compensating time-: this is a number that makes guest card period of validity little longer than the real period to confirm guest can pass in his living term.

E.g. here is 20, when guest check in 12:00 to next day 13:00, the real rang in his card will be 11:40 to next day 13:20.

TM lock- use TM card

IC lock- use SLE4442 card

AT lock- use T5557 RFID card

TI lock- use TI card

RFID(Mifare)- use Mifare 1K card.

Note: It requires restart software for switching to another lock type.

For USB port encoder, select COM Port。

Click Apply, close it and next running the above setting effect.

Refresh- Make the window updating, show the new content, pressing F5 is the same function.

Check-In- Issue card for guest.

Group Check-In-Issue card for some guests who are a family or a team when they check in at a same time.

Change Status- Change room’s status, there are 6 statuses, once you select one to change, the room’s icon is changed instantly.

Lock Events- Collect reading cards and unlocking events of the room, when you select rooms, it’s available.

Open it now!- Remote open the door by computer.

Passage mode On- Make rooms at passage status and they will keep unlocking all the time although deadbolt.

Passage mode off- Make rooms’ passage status off and they will be locked

Arrange by Room NO.- Arrange rooms by room’s NO.

Arrange by Status- Arrange rooms by their status.

When a room is selected, these menus are available.

Deadbolt override-If Selected, this option will be auto selected when issue guest card and all other functions  cards. Still user can cancel select it to off this function for a card.

Detect not closed fully warning-

3 beeps in 3 sec plus red light- there are 3 beeps in a break if door latch not closed properly.

Always beeps plus red light- there are continuous beeps

Red light only- there is red light flash only,

No alarm- Nothing happen when door is not closed properly.

Motor running time- 0.20sec to 12.60sec, default 0.20sec (we do not suggest you adjust it to over 0.40sec, it may cause motor damaged.)

More in 1 Guest card- The maximum rooms in one card, default is 4, can be changed in configuration table

Note: The two above can’t be changed here, you can modify in configuration table.

Common door function- switch of common door function, if Off, there is no related menu showed.

Elevator function- switch of elevator function(hardware support required)

Multi-cards for 1 room-.switch of several cards for 1 room

Fast revoke (guest card)-when it is no, when you issue a unblank guest card, the soft will warn you firstly.

Passage function- when it is show ,the passage option will appear when issue guest card. If guest card is seleted passage On, it will make the door in always open status after reading .

You can define all rooms status color as whichever you like, there are many kinds of colors here.

Server IP address- If the Xentral server is set up on your computer with Hotel Lock System software, you are the server and client, so, you must select I am the server, then this item is unavailable. If  Xentral is set up on other computer, you are not server but client only, you need to search server’s IP and fill in here.

Read null card-Max times lock read a null card, when over it, lock will card to lock will give an alarm. You can change in range of 4 to 10.

Unlocking delay- Time of unlocking door, range is 1 to 25 sec.

Event save mode-

Covered by latest- When lock events in lock is over the max that lock can contain, the old will be leave behind automatically and save the new.

Alarm for full- when events is full, there will be an alarm to warning you.

Warning:

Registered version will show ‘Registered’ on the title of soft.

If you have not finished register as the above, you can not go on following setting.

All your operate will be report ‘ Operate not support!’

This is to make locks connect with you computer and make up of a LAN.

1. Select Building from building name.

2. Define the room which floor it belongs to, room’s name, area, select room type.

3. Select the Hotel Lock system type. Here select TCP/IP Online. Then it will switch to TCP/IP setting automatically

If your hotel has public place such as Club, swimming pool etc, only when you have installed Xeeder hotel lock products, the common doors function is able to use

Here you should define each common doors name and description so that you can know which door belongs to which place easily.

e.g. hotel has 2ype common doors, 1 swimming pool, 1 Sauna. All of these places have installed Xeeder hotel lock system hardware, then you can edit its name first in the common doors setting window.

Lock Type- Select lock type, here you should select TCP/IP Online, then it will switch to TCP/IP message to set information.

As set lock IP, input MAC and IP address, select events save mode and fill in others. Then click Set to confirm. Save, continue to set next.

If you select default common door, when you issue guest card common door you have select will automatically add, but you can change.

All common doors showed here is the list you finished when build common doors

All doors you want to filter guest can install Xeeder hotel lock or wall reader to let it become a common door.

These public place may include free open place and valued service place.

Mac add- Every locks has only one Mac, and they are different with others’, you should fill in here

Final IP- As the Mac, they are all different, you should set an IP for every lock, it should keep in step with computer’s IP.

e.g. your computer’s IP is 192.168.0.136, lock IP can be set from 192.168.0.1 to 192.168.0.254 except 192.168.0.136, avoiding clash. If these IP have been occupied by others, you must change or add new IP for your computer.

Event save mode- Two different lock saving events mode, as we described ahead.

Unlocking delay(sec)- unlocking time.

Fill in the Begin Date and time, Expiry Date and time. Input the guest’s name, click Issue to finish. The room’s check-in card you issued before has no effect from now on.

If you don’t know the card has content or not, before issued Check-out car, you can click verify to confirm.

By card NO.

step1:Click Select, all the card issued before will be show in a form, you can easily find lost card by selecting card type and issued time.

e.g. You can select guest card, issued on 17th, July,2009, then records according with you show in form. Then close it .

step2: click issued, finish.

Invalidate it- make the lost unable work

Recover it- make the lost able to work again.

Step2: Input the nights guests want to living in(default is 3 nights), fill in the Guests name, passport, specific time of checking in and checking out. Finishing, issue card.

More in 1- Issue multi-door in one card, so, the issued card can open multi-room. If selected, there will be as following:

You can select rooms from Room list.

Step1: Select room the guests want to check in from Room list. Click Room list, all rooms is showed in form, when you click every room, its status is showed on the top. you can also search room quickly, inputting name of the room, building or floor. After finding the room, double click it, close.

E.g. Today is 17th July,2009.103 guest empty come to reception and ask extend 1 days(Origin is 7/18).

So the new check out date should be 19thJuly,2009(7/19)

See the car’s content to confirm if this is the one you want to revoke or not.

Select card type and issued date, all items according with you will show, quickly search the card issued before.

This card has time limited, you should fill in specific time in Begin Date and Expiry Date. Input holder’s name. Then, click Issue . Issuing information shows at the bottom:

Select areas(can contain several areas) and time of validity, default is 1 year. Fill in the Time Bucket of every day and holder’s name.

Same as master card. Select buildings(can contain several buildings) and time of validity, default is 1 year. Fill in the Time Bucket of every day and holder’s name.

The selected common doors will show green background color which means it will become an auto common door when issue guest card. In this example, Sauna room and Swimming Pool had been selected as auto common doors. Guest can pass them by read their own guest (room) card.

But other place is not selected and guest can not pass them.

Note: Here you should not set a same IP as Guest rooms, because one room can’t be Guest room and public place at the same time.

Select the room and click adjust time, lock’s time will be the same as the current time.

e.g. Room 204 has lost power 2 hours, then select it, and click Adjust time.

is at the bottom.

Red background room is busy.