###### YG200 (Serial No.        )

###### Specification Sheet

[  ]  for Estimation

[  ]  for Production

#### To :

YAMAHA MOTOR CO., LTD.

IM Company

[ A divisional operation of YAMAHA MOTOR CO., LTD. ]

Apr. 15, 2004	   Ver. 1.50

# 1.	Device configuration

## 1.1	Machine layout

Model code :

F/S :  Head selection, F (FNC heads) or S (Standard heads)

250 :  PCB width, Max. 250mm only

R/L :  Conveyor entrance, R (Entrance on Right) or L (Entrance on Left)

F/R :  Conveyor reference, F (Front side) or R (Rear side)

Type :  Layout type, #1, #2, #3, or #4 (Please refer following figures.)

YG200 – [  ] – 250 – [  ] – [  ] – [  ]

#1               #2               #3               #4

[      ] : Fill the “Adoption” box with either “○” or “”.

| Type | Model code | Maximum PCB size | Conveyor entrance | Conveyor reference | Adoption |
| --- | --- | --- | --- | --- | --- |
| #1 | YG200 - F/S – 250 – R - F | L330mm * W250mm | Right | Front |  |
| #2 | YG200 - F/S – 250 – L – F |  | Left |  |  |
| #3 | YG200 – F/S – 250 – R – R |  | Right | Rear |  |
| #4 | YG200 – F/S – 250 – L – R |  | Left |  |  |

## 1.2	Built-in initial and optional device

[  ●  ] : Initial installed equipments

[      ] : In case of the adoption, fill the blank box with either “○” or “”.

[   EA.] : In case of the adoption, input the number at the front of “EA. (=each)”.

|  | No. | Device | Adoption |
| --- | --- | --- | --- |
|  | 1.2.01 | Serial No. machine body (including controller) | ● |
|  | 1.2.02 | Head selection | 4 rows of 6 in-line FNC heads |  |  |
|  |  |  | 4 rows of 6 in-line Standard heads |  |  |
|  | 1.2.03 | Conveyor entrance selection | Ini. | Right |  |  |
|  |  |  | Op. | Left (reverse transfer Left to Right) |  |  |
|  | 1.2.04 | Conveyor reference selection | Ini. | Front |  |  |
|  |  |  | Op. | Rear (rear side positioning) |  |  |
|  | 1.2.05 | Nozzle variation change : 72F ( 79F (12 nozzles) |  |
|  | 1.2.06 | Nozzle variation change : 202A ( 209A (advised quantity) |  |
|  | 1.2.07 | Nozzle grade-up : 73F ( 73F-D (12 nozzles) |  |
|  | 1.2.08 | Nozzle grade-up : 203A ( 203A-D (advised quantity) | EA. |
|  | 1.2.09 | 4 high-resolution digital multi cameras | ● |
|  | 1.2.10 | 4 fiducial-mark recognition cameras | ● |
|  | 1.2.11 | Feeder carriage exchange system (Interface only, 4 bays) |  |
|  | 1.2.12 | Non-stop feeder carriage exchange system (Interface only, 4 bays) |  |
|  | 1.2.13 | Feeder carriage 20 positions (Normal type) | EA. |
|  | 1.2.14 | Splicing carriage 20 positions (“Normal type” + installed “Reel holder assy”) | EA. |
|  | 1.2.15 | Feeder floating detection (front *2 units & rear *2 units) |  |
|  | 1.2.16 | Area sensor (front *1 unit & rear *1 unit) |  |
|  | 1.2.17 | 2 Main stoppers (for PCB positioning) | ● |
|  | 1.2.18 | 2 Clamp board positioning units | ● |
|  | 1.2.19 | 2 Linkage mechanism push-up units | ● |
|  | 1.2.20 | 2 Matrix type push-units |  |
|  | 1.2.21 | Waiting position sub-stopper (entrance side) | ● |
|  | 1.2.22 | Exit sub-stopper | ● |
|  | 1.2.23 | High-speed soft-stop conveyor | ● |
|  | 1.2.24 | 4 segments conveyor system | ● |
|  | 1.2.25 | Automatic adjustment of conveyor width | ● |
|  | 1.2.26 | Both front & rear sided LCD displays (indicating only) | Ini. |  |  |
|  |  | Both front & rear sided LCD touch-panels (Optional) | Op. |  |  |
|  | 1.2.27 | Both front & rear sided input devices (Keyboard, Mouse, Operation-panel) | ● |
|  | 1.2.28 | Expansion gate signal (between machines in previous and next process) | ● |
|  | 1.2.29 | Gate signal cable between machines | ● |
|  | 1.2.30 | Function to vary XY axis speed by components | ● |
|  | 1.2.31 | Service tools | ● |
|  | 1.2.32 | 3-color signal tower (Warning lights) | ● |

|  | No. | Device | Adoption |
| --- | --- | --- | --- |
|  | 1.2.33 | 3.5 inch floppy disk drive | ● |
|  | 1.2.34 | CD-ROM drive | ● |
|  | 1.2.35 | Safety cover with emergency-stop (both front & rear) | ● |
|  | 1.2.36 | Service fluorescent light (Linked with safety covers, ON, or OFF selectable) |  |
|  | 1.2.37 | Dump station (Recovery conveyor) | Counter type : KGA-M94A0-00 |  |
|  |  |  | Sensor type : KGA-M94A0-10 |  |
|  | 1.2.38 | Additional wiring for stack stick feeders |  |
|  | 1.2.39 | UPS system (excluding servo motors drive) ### As this is a lead-acid battery, be careful when handling it. In case of oversea transportation, it has to be packed separately and applied as dangerous device. It’s necessary to be kept the ambient storage temperature between 50 centigrade to – 15 centigrade. Also, because of the battery service life, the replacement maintenance will be needed roughly every 2 years. |  |
|  | 1.2.40 | Ionizer (ion generator to remove static electricity : both front & rear) |  |
|  | 1.2.41 | Receiving voltage lamp |  |
|  | 1.2.42 | SMEMA interface kit |  |
|  | 1.2.43 | COM-2 port (general communication by using RS-232C ) |  |
|  | 1.2.44 | Power supply voltage selection : AC 3-Phase, +/- 10%, 7.4 kVA ### Cross-sectional area of .each power supply cable conductive : ( 3.5 mm*mm or more, equivalent for AWG #13 (American wire gage) | 200V |  |
|  |  |  | 208V |  |
|  |  |  | 220V |  |
|  |  |  | 240V |  |
|  |  |  | 380V |  |
|  |  |  | 400V |  |
|  |  |  | 416V |  |
|  | 1.2.45 | Power supply frequency selection | 50Hz |  |
|  |  |  | 60Hz |  |
|  | 1.2.46 | Protector selection | Ini. | Circuit protector (Normal type) ### Rated uninterrupted current 16A |  |  |
|  |  |  | Op. | Earth leakage breaker (Sensitivity 15mA type) ### Rated current 15A |  |  |
|  |  |  | Op. | Earth leakage breaker (Sensitivity 30mA type) ### Rated current 15A |  |  |
|  | 1.2.47 | Operating System Language selection | for English & Chinese expression |  |  |
|  |  |  | for English & Japanese expression |  |  |
|  | 1.2.48 | Language expression selection | English |  |
|  |  |  | Chinese (English reversible) |  |
|  |  |  | Japanese (English reversible) |  |

## 1.3	Customized device

[      ] : In case of the adoption, fill the blank box with either “○” or “”.

[   EA.] : In case of the adoption, input the number at the front of “EA. (=each)”.

|  | No. | Device | Adoption |
| --- | --- | --- | --- |
|  | 1.3.01 | Customized nozzles | EA. |
|  | 1.3.02 | Customized nozzles with additional function | EA. |
|  | 1.3.03 | Conveyor extension (either entrance side or exit side) | 150mm |  |
|  |  |  | 250mm |  |
|  |  |  | 300mm |  |
|  | 1.3.04 | Ceramic PCBs supported |  |
|  | 1.3.05 | Small-sized PCBs supported (e.g., L15mm*W15mm) |  |
|  | 1.3.06 | Thin PCBs supported (e.g., T=0.3mm) |  |
|  | 1.3.07 | Conveyor entrance & exit covers |  |
|  | 1.3.08 | Safety covers for feeder carriage |  |
|  | 1.3.09 | Area sensor for full feeder covers |  |
|  | 1.3.10 | Both front & rear sided anti-static electricity covers |  |
|  | 1.3.11 | Changing signal tower height |  |
|  | 1.3.12 | Changing signal tower display pattern |  |
|  | 1.3.13 | Warning buzzer addition |  |
|  | 1.3.14 | Power-ON pilot lamp |  |
|  | 1.3.15 | Transport height of 930mm supported |  |
|  | 1.3.16 | 10,000 Class Cleanliness supported |  |
|  | 1.3.17 | Additional safety devices & functions based on customer’s standard ### for out of EU region |  |
|  | 1.3.18 | Specified color | Monotone color |  |
|  |  |  | Two-tone color |  |

The matters worthy of special mention

[1]

[2]

[3]

[4]

[5]

## 1.4	Attached optional device (Accessories)

[   EA.] : In case of the adoption, input the number at the front of “EA.(=each)”.

|  | No. | Device | Adoption |
| --- | --- | --- | --- |
|  | 1.4.01 | Additional feeder carriage 20 positions (Normal type) | EA. |
|  | 1.4.02 | Additional splicing carriage 20 positions (“Normal type” + installed “Reel holder assy”) | EA. |
|  | 1.4.03 | Reel holder assy (Splicing rack unit only) : KV8-M3R00-00 | EA. |
|  | 1.4.04 | Tape dump box for floor placed (for YG200 exclusive) : KU5-M3600-00 | EA. |
|  | 1.4.05 | Tape dump box for feeder carriage 20 positions: KV8-M3600-02 | EA. |
|  | 1.4.06 | Tape dump box with automatic cutter (for YG200 exclusive) : K??-M????-?? | EA. |
|  | 1.4.07 | Tape connector for splicing : KJ3-MY020-10 | EA. |
|  | 1.4.08 | Joint tape 8mm width (1,000 pieces pack) : KJ3-MY031-00 | EA. |
|  | 1.4.09 | Joint tape 12mm width (1,000 pieces pack) : KJ3-MY032-00 | EA. |
|  | 1.4.10 | Joint tape 16mm width (500 pieces pack) : KJ3-MY033-00 | EA. |
|  | 1.4.11 | Joint tape 24mm width (500 pieces pack) : KJ3-MY034-00 | EA. |
|  | 1.4.12 | Joint tape 32mm width (500 pieces pack) : KJ3-MY035-00 | EA. |
|  | 1.4.13 | Joint tape 44mm width (500 pieces pack) : KJ3-MY036-00 | EA. |
|  | 1.4.14 | Joint tape 56mm width (500 pieces pack) : KJ3-MY037-00 | EA. |
|  | 1.4.15 | Air dryer and oil separator unit : K98-M3900-00, Sun drain | EA. |
|  | 1.4.16 | Filter element (spare) : K98-M3903-00 | EA. |
|  | 1.4.17 | Spare parts kit selection | for FNC heads (72F arrangement) : KGT-M8900-00 | EA. |
|  |  |  | for FNC heads (79F arrangement) : KGT-M8900-10 | EA. |
|  |  |  | for Standard heads (202A arrangement) : KGT-M8900-50 | EA. |
|  |  |  | for Standard heads (209A arrangement) : KGT-M8900-60 | EA. |
|  | 1.4.18 | Feeder stand | EA. |
|  | 1.4.19 | Pick-up position inspection jig ### (KJ3-M34E0-00, Jig feeder pick pos.) + (KJ3-MJA00-00, Tool case assy) | EA. |

## 1.5	Attached feeders

[   EA.] : In case of the adoption, input the number at the front of “EA.(=each)”.

|  | No. | Device | Adoption |
| --- | --- | --- | --- |
|  | 1.5.01 | CL tape feeder 8mm Standard 7 inch (4mm pitch) | EA. |
|  | 1.5.02 | CL tape feeder 8mm Standard 15 inch (4mm pitch) | EA. |
|  | 1.5.03 | CL tape feeder 8mm Thin (T=0.3mm) 7 inch (4mm pitch) | EA. |
|  | 1.5.04 | CL tape feeder 8mm Thin (T=0.3mm) 15 inch (4mm pitch) | EA. |
|  | 1.5.05 | CL tape feeder 8mm 7 inch for 1005 chip (2mm pitch) | EA. |
|  | 1.5.06 | CL tape feeder 8mm 15 inch for 1005 chip (2mm pitch) | EA. |
|  | 1.5.07 | CL tape feeder 8mm 7 inch for 0603 chip (2mm pitch) | EA. |
|  | 1.5.08 | CL tape feeder 8mm 15 inch for 0603 chip (2mm pitch) | EA. |
|  | 1.5.09 | Splicer for CL 8mm 7 inch : KW1-M1G00-00 | EA. |
|  | 1.5.10 | Splicer for CL 8mm 15 inch : KW1-M1H00-00 | EA. |
|  | 1.5.11 | CL tape feeder 12mm 15 inch | EA. |
|  | 1.5.12 | CL tape feeder 16mm 15 inch | EA. |
|  | 1.5.13 | CL tape feeder 24mm 15 inch (Roll-up type) | EA. |
|  | 1.5.14 | CL tape feeder 32mm 15 inch (Roll-up type) | EA. |
|  | 1.5.15 | CL tape feeder 44mm 15 inch (Roll-up type) | EA. |
|  | 1.5.16 | CL tape feeder 56mm 15 inch (Roll-up type) | EA. |
|  | 1.5.17 | Tape feeder 32mm 15 inch for Adhesive tape | EA. |
|  | 1.5.18 | Tape feeder 72mm (Roll-up type) | EA. |
|  | 1.5.19 | Bulk cassette feeder 1005C(T=0.5mm) TDK-made | EA. |
|  | 1.5.20 | Bulk cassette feeder 1005R(T=0.3mm) TDK-made | EA. |
|  | 1.5.21 | Bulk cassette feeder 1608C(T=0.8mm) TDK-made | EA. |
|  | 1.5.22 | Bulk cassette feeder 1608R(T=0.4mm) TDK-made | EA. |
|  | 1.5.23 | Bulk cassette feeder 2012C(T=1.2mm) TDK-made | EA. |
|  | 1.5.24 | Bulk cassette feeder 2012C(T=0.8mm) TDK-made | EA. |
|  | 1.5.25 | Bulk cassette feeder 2012R(T=0.6mm) TDK-made | EA. |
|  | 1.5.26 | Multi stick feeder (without track) | EA. |
|  | 1.5.27 | Track for multi stick feeder | EA. |
|  | 1.5.28 | Track for special component (component height 2.5 ~ 5.0mm) | EA. |
|  | 1.5.29 | Track for special component (stick tube height 10.6 ~ 14.8mm) | EA. |
|  | 1.5.30 | Stick pan for multi stick feeder | EA. |
|  | 1.5.31 | Stack stick feeder (for special component) | EA. |
|  | 1.5.32 | High-speed stack stick feeder (standard SOP, except for special component) | EA. |
|  | 1.5.33 | High-speed stick feeder (standard SOP, except for special component) | EA. |
|  | 1.5.34 | High-speed stick feeder (PLCC20, PLCC40) | EA. |

# 2.	Technical feature

## 2.1	Appearance

### The above figure shows the appearance of the standard configuration.

## Basic configuration

| Dimension | L1,950 * W1,408 * H1,850mm |
| --- | --- |
| Weight | Approx. 2,080kg |
| Air source | 0.55MPa or more, Max. 400L/min(ANR), in clean and dry state Recommend using over 8mm inside-diameter air hose, because of the flow. |
| Power supply | Type / voltage | AC 3-phase 200/208/220/240/380/400/416V ±10% |
|  | Frequency | 50Hz/60Hz |
|  | Rating | 7.4kVA |
| Average power consumption | 1.0 kW (When running normal condition) |
| Supply cable | Cross-sectional area of each conductive cable : ( 3.5 mm*mm or more, equivalent for AWG#13 (American wire gage) |
| Environmental condition | Noise | 1500V、1micro-sec or less, diverting strong-noise units |
|  | Temperature | Operating : 15 ~ 35 C-degree Accuracy-insuring : 20 ~ 28 C-degree |
|  | Humidity | 20～90%, with non-dew condenses |
|  | Atmosphere | Avoiding dust and dirt |
|  | Floor | To be flat and stiff enough to be vibrated at operating. Especially, wooden floor can’t be applicable. |
| Conveyor speed | 50 ~ 550mm/sec : 60Hz power supply (variable speed setting) 50 ~ 450mm/sec : 50Hz power supply (variable speed setting) * Conveyor speed may be changed by PCB weight etc. |
| Safety function | Double runaway prevention with software-limit and hardware-limit (XY axes) Safety cover interlock Servo-error detection (over-load, over-current, feedback-error, etc.) |
| Warning light signal mode | Red lamp | CPU NG/Emergency stop, Safety-cover (Interlock) |
|  | Yellow lamp | Pickup error, Out of components, Conveyor time out |
|  | Green lamp | In automatic operation |
| Data Mounting point Components type PCB file Fiducial type Input method | 10,000 points (reduction by PCB, Fiducial, block data) 250 type/PCB Max. 255 PCB/machine 500 pair/PCB (in case of 2 point fiducial) Manual data input by machine console (key-board and mouse, optional touch-panel) and/or MSP (maintenance support pendant unit) |
| Min. setting unit | X, Y, Z axes : 0.001mm R axis : 0.001 degree |
| Interface | LAN X1 |
| External memory | 3.5 inch FDD MS-DOS format 1.44MB/720KB ｘ 1 unit 512MB Flash card (save for operation program, PCB, feeder, vision, machine info., and production history ) External memory (PC) by LAN communication |
| Transfer height | 900mm +/- 10mm (from floor to transfer-belt) |

## 2.3.  Machine specification

### 2.3. 1.	Axis specification

| Item | Distinction | Specification |
| --- | --- | --- |
| Nos. of total axes |  | 20 axes |
| Axis configuration | Main drive AC servo motor | X *4, Y *2 |
|  | Head drive AC servo motor | R *4, Z *4 |
|  | Conveyor width drive AC servo motor | W *4, |
|  | PCB transfer drive AC servo motor | YT *2 |

### 2.3. 2. 	Standard equipment

| Unit | Q’ty | Unit | Q’ty |
| --- | --- | --- | --- |
| Machine body (incl. controller) | 1 set | Linkage mechanism push-up unit | 2 sets |
| 3.5 inch floppy disk drive | 1 set | CCD camera for fiducial recognition | 4 sets |
| Operation support panel | 2 sets | Standby position sub-stopper | 1 set |
| 6 in-line multi head | 4 sets | Exit position sub-stopper | 1 set |
| PCB transfer system (YT axis & Conveyor) | 1 set | Warning light (tricolor type) | 1 set |
| Clamp board positioning system | 2 sets | CD-ROM drive (for Program installation and/or update) | 1 set |
| Key board & Mouse for data input | 1 set | Safety cover with emergency-stop (both front & rear) | 1 set |
| LCD display panel | 2 sets | Conveyor width auto adjusting | 1 set |

## 2.4.	Recognition System

### 2.4.1	CCD camera for fiducial mark recognition

● Condition of fiducial mark

| Item | Remark |
| --- | --- |
| Purpose | Fiducial mark detection, Bad mark detection, Teaching |
| Mark recognition | Circle shape 1~2 mm diameter Square shape 1~2 mm * 1~2 mm, Diamond shape 1~2 mm * 1~2 mm The contrast between marks and PCB surface must be clear. The surface of the mark must be no scratches, etc. The reflective object can be either on the mark side or periphery. |
| Surface material | Copper foil, solder plating, gold plating |
| PCB material | Glass-fiber reinforced epoxy resin is the most stable. White ceramic and glossy material may be inadequate. |
| Scan area | There must be no resist, silk-screen printing, or other patterns within a 4 mm * 4 mm square from the mark center. |
| Mark setting position | Two (2) or four (4) points on diagonal positions in the PCB will be suitable. Same point can not be used. |

### 2.4.2	Camera for component recognition : applicable component

- Mountable component size

| Camera | FOV : Field of view (mm * mm) | Min. lead pitch (mm) | Component size (mm * mm) |
| --- | --- | --- | --- |
| Multi-view camera for sequential recognition | 14*14 | 0.4 | 0603chip ~ 14*14 |

### Remark

The FOV (field of view) of the rear multi-view camera must be same as front one. Component size means outer dimension including the leads. ### Depending on the component size, the mounting speed may be reduced. In case of out-of-spec components, please consult with YAMAHA staff.

## 2.5	Head section / YG200-S

### 2.5.1	Configuration

| Up-down drive method | Pneumatic cylinder + AC servo motor (Z axis) |
| --- | --- |
| Rotation drive method | AC servo motor (R axis) |
| Pick-up error detection | Vacuum sensor check (256 level digital setting) and component shape recognition |
| Mounting angle | 0 ~ +/- 180 degree (0.01 degree step) |
| Head arrangement | 6 in-line multi head (Nozzle-change type * 6 ) * 4 sets |
| Nozzle type | 4 types (standard) |

## 2.6	YG200-S Nozzle combination

2.6.1  Nozzle specification

|  | Applicable component |
| --- | --- |
| Type 201A | 0603 ~ 1005 |
| Type 202A | 1608 ~ 3216 |
| Type 203A | 4532 etc. ~ SOP |
| Type 206A | Cylindrical chip (MELF) |

2.6.2  Nozzle quantity ( standard : total 6 ea ) for one head

|  | Standard |
| --- | --- |
| Type 201A | (6) ea |
| Type 202A | (6) ea |
| Type 203A |  |
| Type 206A |  |

2.6.3  Combination

|  | Type 201A | Type 202A | Type 203A | Type 206A |
| --- | --- | --- | --- | --- |
| Head 1 | <Select> | <Select> | (Hand) | (Hand) |
| Head 2 | <Select> | <Select> | (Hand) | (Hand) |
| Head 3 | <Select> | <Select> | (Hand) | (Hand) |
| Head 4 | <Select> | <Select> | (Hand) | (Hand) |
| Head 5 | <Select> | <Select> | (Hand) | (Hand) |
| Head 6 | <Select> | <Select> | (Hand) | (Hand) |

<Select>	: by selection of either Type 201A nozzle or Type 202A nozzle

(Hand)	: by using hand-operated change, for using optional and/or customized nozzles

Note

About the <Select> in the above chart, either Type 201A nozzle or Type 202A nozzle should be installed. If both nozzles would be held, another nozzle should be changed by hand-operation each other. About the (Hand) in the above chart, every option and/or customized nozzle should be changed by using hand-operation. In case of two(2) or more Type 203 and/or 206 nozzles installation into the heads, the component size may be limited.

## 2.7	Head section / YG200-F

### 2.7.1	Configuration

| Up-down drive method | Pneumatic cylinder + AC servo motor (Z axis) |
| --- | --- |
| Rotation drive method | AC servo motor (R axis) |
| Pick-up error detection | Vacuum sensor check (256 level digital setting) and component shape recognition |
| Mounting angle | 0 ~ +/- 180 degree (0.01 degree step) |
| Head arrangement | 6 in-line multi head (Index type * 3 + nozzle-change type * 3 ) * 4 sets |
| Nozzle type | 4 types (standard) |

Fig.  Index head  (Bevel-gear-side layout)

### 2.7.2	ＹG200－Ｆ  Nozzle type for Index head [ FNC (type) nozzle ]

### (Head Nos. 2, 4 and 6)

| Index nozzle holder Nos. | Standard equipped nozzle |
| --- | --- |
| 1 | Type 201F |
| 2 | Type 202F |
| 3 | Type 203F |

Note

Index heads are installed at head position Nos. 2, 4 and 6. {Head position Nos. are numbered from right side (when viewed from the front), as 1, 2, 3, 4, 5 and 6} The nozzle 201F, 202F and 203F are same as the nozzle 71F, 72F and 73F.

## 2.8	YG200-F Nozzle combination

2.8.1  Nozzle specification

|  | Applicable component |
| --- | --- |
| Type 201A / 201F | 0603 ~ 1005 |
| Type 202A / 202F | 1608 ~ 3216 |
| Type 203A / 203F | 4532 etc. ~ SOP |
| Type 206A | Cylindrical chip (MELF) |

2.8.2  Nozzle quantity ( standard : F-type 9ea, A-type 3ea ) for one head

|  | Standard |
| --- | --- |
|  | F | A |
| Type 201 | 3 ea | (3) ea |
| Type 202 | 3 ea | (3) ea |
| Type 203 | 3 ea |  |
| Type 206 |  |  |

2.8.3  Combination

|  | Type 201 | Type 202 | Type 203 | Type 206 |
| --- | --- | --- | --- | --- |
| Head 1 | [Select] | [Select] | (Hand) | (Hand) |
| Head 2 | <F> | <F> | <F> |  |
| Head 3 | [Select] | [Select] | (Hand) | (Hand) |
| Head 4 | <F> | <F> | <F> |  |
| Head 5 | [Select] | [Select] | (Hand) | (Hand) |
| Head 6 | <F> | <F> | <F> |  |

[Select]	: by selection of either Type 201A nozzle or Type 202A nozzle

<F>	: by using FNC type nozzle

(Hand)	: by using hand-operated change, for optional and/or customized nozzles.

FNC type nozzles are installed into index Head Nos. 2, 4 and 6 above <F> position.

ANC type and/or customized nozzles are installed into nozzle-change Head Nos. 1, 3 and 5 above [Select] and (Hand) positions.

Note

About the [Select] in the above chart, Either Type 201A nozzle or Type 202A nozzle should be installed. If both nozzles would be held, another nozzle should be changed by hand-operation each other. In case of two(2) or more Type 203 and/or 206 nozzles installation into the heads, the component size may be limited. The [Select] and (Hand) in the above chart means a ANC (type) and/or customized nozzle for the nozzle-change type head, and the [F] in the above chart means an FNC (type) nozzle for the index type head.

# 3.	Specification

## 3.1	Adaptive PCB specification

### 3.1.1　PCB dimension (shape / size) for <Front side positioning>

| Direction | PCB shape |
| --- | --- |
| R -->> L (standard) |  |
| L -->> R (optional) |  |

| Machine type | Q’ty of Multi-view camera | Max. PCB size (L*W) | Min. PCB size (L*W) | Q’ty of Feeders |
| --- | --- | --- | --- | --- |
| M type | 2 | 330mm * 250mm | 50mm * 50mm | 80 |

Remark

C: Flat section, 30 mm D: Oval (slot) hole length In case of D > 3 mm, the fixed type sub-stopper should be required.

### 3.1.2	PCB material / thickness

Glass-fiber reinforced epoxy resin

(In case of other kind of materials, please consult with YAMAHA staffs.)

0.4～3.0mm

### 3.1.3	PCB warping

Upward warping :		0.5mm (max.)

Downward warping :	1.0mm (max.)

Remark

If a PCB warped greater than the values given above (especially in the upward direction) is mounted, the mounting accuracy can drop remarkably.

### 3.1.4	PCB weight

0.65 kg (max.)

### 3.1.5	PCB upper/lower components restrictions

PCB upper side

Standard head :	Height of 6.5mm or less from PCB upper surface

FNC head :		Pre-mounted (before PCB conveyance) component height is 4mm or less.

PCB lower side

Height of 25mm or less from PCB lower face

But, there must be no component for 3mm from both ends of PCB width.

# 3.	Specification

## 3.1	Adaptive PCB specification

### 3.1.1　PCB dimension (shape / size) for <Rear side positioning>

| Direction | PCB shape |
| --- | --- |
| R -->> L (standard) |  |
| L -->> R (optional) |  |

| Machine type | Q’ty of Multi-view camera | Max. PCB size (L*W) | Min. PCB size (L*W) | Q’ty of Feeders |
| --- | --- | --- | --- | --- |
| M type | 2 | 330mm * 250mm | 50mm * 50mm | 80 |

Remark

C: Flat section, 30 mm D: Oval (slot) hole length In case of D > 3 mm, the fixed type sub-stopper should be required.

### 3.1.2	PCB material / thickness

Glass-fiber reinforced epoxy resin

(In case of other kind of materials, please consult with YAMAHA staffs.)

0.4～3.0mm

### 3.1.3	PCB warping

Upward warping :		0.5mm (max.)

Downward warping :	1.0mm (max.)

Remark

If a PCB warped greater than the values given above (especially in the upward direction) is mounted, the mounting accuracy can drop remarkably.

### 3.1.4	PCB weight

0.65 kg (max.)

### 3.1.5	PCB upper/lower components restrictions

PCB upper side

Standard head :	Height of 6.5mm or less from PCB upper surface

FNC head :		Pre-mounted (before PCB conveyance) component height is 4mm or less.

PCB lower side

Height of 25mm or less from PCB lower face

But, there must be no component for 3mm from both ends of PCB width.

## 3.2	Mountable component size

| Nozzle type | Example of mountable component (unit : mm) |
| --- | --- |
| Type 201A/201F | Resistor / ceramic capacitor | L0.6*W0.3 ~ L1.0*W0.5 |
| Type 202A/202F Type 209A/209F | Resistor | L1.6*W0.8*T0.5 ~ L3.2*Ｗ1.6*T1.25 |
|  | Ceramic capacitor | L1.5*W0.8*T0.5 ~ L3.2*Ｗ1.6*T1.25 |
|  | Cylindrical chip (MELF type) | L2.0*Dia.1.25 ~ L3.45*Dia.1.35 |
|  | Tantalum electrolytic capacitor | L2.9*W1.6*T1.6 |
|  | Mini-mold transistor | L2.9*W1.5*T1.1 |
| Type 203A/203F | Ceramic capacitor | L3.2*W2.5*T1.5 ~ L5.6*W5.0*T1.9 |
|  | Tantalum electrolytic capacitor | L4.7*W2.6*T2.1 ~ L7.3*W4.3*T2.8 |
|  | Aluminum electrolytic capacitor | L4.3*W4.3*T5.7 * L6.6*W6.6*T5.7 |
|  | Chip film capacitor | L7.3*W5.3*T3.25 |
|  | Chip Inductor | L3.2*W2.5*T2.0 ~ L4.5*W3.2*T3.2 |
|  | Semi-variable resistor | L4.5*W3.8*T2.4 |
|  | Power transistor | L4.6*W2.6*T1.6 |
|  | SOP | L5.0*W4.5*T1.5 ~ L12.6*W5.7*T1.5 |
|  | PLCC | Mold section 5.0*5.0 ~ 15.0*15.0 |
|  | QFP / BGA / CSP | Mold section 5.0*5.0 ~ 16.0*16.0 |
| Type 206A | Cylindrical chip (MELF type) | L2.0*Dia1.25 ~ L6.0*Dia2.5 |

| Component height | 6.5mm or less |
| --- | --- |
| Component mounting interval | Chip 0.5mm or more (including X, Y and angle value) But, in case of 1005 or less size chip component mounting (around neighboring component that is the same height or more lower), 0.25mm or over. (including X, Y and angle value) |
|  | SOP 0.5mm or more (in case of mold section 14mm*14mm or less, including X, Y, and angle value, in lead direction) |

Remark

In case of 20 points feeder exchange carriage, the correction by teaching operation is necessary.

## Feeder installation configuration

| Feeder type | Required feeder position equivalent to tape feeder 8mm | Applicable No. of Feeder Position |
| --- | --- | --- |
| Tape feeder 8mm, Bulk cassette feeder | 1 | 1-20 |
| Tape feeder 12mm, 16mm, 24mm | 3 | 2-19 |
| Tape feeder 32mm | 4 | 3-18 |
| Tape feeder 44mm | 5 | 3-18 |
| Tape feeder 56mm | 6 | 4-18 |
| Wide multi-stick feeder | 10 | 4-14 |

Note

The above feeder conversion number may differ according to the installation combination. The above available position area shows the guidance at the front-side feeder plate. About the rear-side feeder plate, it is similar to above chart. In case of the pick-up position correction by teaching operation, available position area may decrease. These bulk feeders can be fitted Max. six (6) units per one-side in a machine. If seven (7) or more units are needed, the additional pneumatic line should be installed as customized specification. Please consult with YAMAHA staff.

## 3.4	Signal specification

### 3.4.1	Signal cable for previous and next devices

|  | Discrimination | Remark |
| --- | --- | --- |
| A type | Standard GATE mode | For YAMAHA hitherto models and/or other-brand machines connection |
| B type | SMEMA mode | Based on SMEMA standard |
| C type | Advanced GATE mode | For YAMAHA X & Xg series connection |

Note

By using software setting, the signal hand-shake specification can be switched.

|  | 5ｍ | 10ｍ |
| --- | --- | --- |
| X -->> X | ea | ea |
| Y -->> X | ea | ea |
| X -->> Y | ea | ea |

Note

The [-->>] in the above chart means the direction from previous machine to next machine. The [X] in the above chart means YAMAHA X & Xg series machine, and [Y] means YAMAHA hitherto machine and/or other-brand machine. In case of other-bland machine, please consult with YAMAHA staff.

### 3.4.2	Connector details

### Next Interface (from this machine to the next machine)

Connector：AMP 206043-1 (14Pin Receptacle type)

| Pin No. | Signal name | Input/Output type | Signal name |
| --- | --- | --- | --- |
| 1 | BUSY IN (+V24) | +V24 | PCB carry-in condition signal |
| 2 | BUSY IN (N1120) | PNP input |  |
| 3 | BA OUT (T1832) | Relay contact (conduction) | PCB carry-out request signal |
| 4 | BA OUT (T1832) | Relay contact (conduction) |  |
| 5 | - |  |  |
| 6 | - |  |  |
| 7 | - |  |  |
| 8 | - |  |  |
| 9 | UR OUT (T1833) | Relay contact (conduction) | Running mode output |
| 10 | UR OUT (T1833) | Relay contact (conduction) |  |
| 11 | LR IN (+24V) | +V24 | Running mode input |
| 12 | LR IN (N1125) | PNP input |  |
| 13 | COUNT RESET (+24V) | +V24 | COUNT RESET signal input |
| 14 | COUNT RESET (N1123) | PNP input |  |

### Previous Interface (from this machine to previous machine)

Connector：AMP 206043-1 (14Pin receptacle)

| Pin No. | Signal name | Input/Output type | Signal name |
| --- | --- | --- | --- |
| 1 | BUSY OUT (T1831) | Relay contact (conduction) | PCB carry-in condition signal |
| 2 | BUSY OUT (T1831) | Relay contact (conduction) |  |
| 3 | BA IN (+24V) | +V24 | PCB carry-out request signal |
| 4 | BA IN (N1122) | PNP input |  |
| 5 | - |  |  |
| 6 | - |  |  |
| 7 | - |  |  |
| 8 | - |  |  |
| 9 | UR IN (+24V) | +V24 | Running mode input |
| 10 | UR IN(Ｎ1124) | PNP入力 |  |
| 11 | LR OUT(T1837) | Relay contact (conduction) | Running mode output |
| 12 | LR OUT(T1837) | Relay contact (conduction) |  |
| 13 | - |  |  |
| 14 | - |  |  |

### 3.4.3  Gate signal specification details

| Receptacle Connector | Specification |
| --- | --- |
| NEXT | (Transfer-out permission signal from next machine) Signal style 1. DC24V 2. PCB transfer-out permission signal input 13. DC24V 14. Count reset signal input [PCB transfer-out permission signal input : Receiving signal from next machine] When between “1. <=> 2.” are electrified (closed), this machine will carry out PCB in case of the mount completed. [Counter reset signal input : PCB carry out counter number reset signal from next machine] By setting the maximum PCB number into this counter, this machine will become on stand-by to carry out PCB at the full-count for the extension time of the next machine, for example, in case of un-loader lack change. Then, when between “13. <=> 14.” are electrified (closed), this machine will re-start the PCB transfer-out and reset the counter. (The “1. <=> 2.”electrified plug-connecter is delivered together with this machine for accessories.) The signal from next machine should be the relay output (Dry-contact : No-voltage type) Refer to following figure in the next page. |
| PREVIOUS | (Transfer-out request signal to previous machine) Signal style 1. PCB transfer-out request signal output 1 (Relay contact : No-voltage type) 2. PCB transfer-out request signal output 2 (Relay contact : No-voltage type) [PCB transfer-out request signal output : Sending signal to previous machine] When this machine is ready to execute the coming routine, between “1. <=> 2.” are electrified (closed) as a PCB request signal. (The plug-connecter is delivered together with this machine for accessories.) Refer to following figure in the next page. |

### NEXT INTERFACE

### PRIVIOUS INTERFACE

# 4.	Software : YGOS

The “YGOS” is right for a line that contains YAMAHA Xg series mounters exclusively, because of the Library data style (XML format) and LAN communication. In case of the combination with YAMAHA X series mounters and/or YAMAHA hitherto models, the “YVOS X” is easier than the “YGOS” for use.

| Item | Application |
| --- | --- |
| YGOS Basic Software (contents : Offline single PCB data Optimizing and Editing, Printing #1) | set |
|  | Hard-key type selection | USB | Conventional |
|  | In case of Windows 98/Me and/or 2000, both USB type and Conventional type can be available. In case of Windows NT4.0, only Conventional type can be available. |  |  |
| Data Conversion |  |
| Line Data Distribution & Optimizing |  |
| Communication software (Software only : for LAN & RS232C connection) |  |
| LAN Connection (Ethernet) | Line control (including “Communication software” and “Line Data Distribution & Optimizing”) |  |
|  | LAN card (General commercial goods for PC) | (By user) |
|  | LAN cable (General commercial goods for PC) | (By user) |
|  | Switching HUB (General commercial goods for LAN) | (By user) |
| RS232C Connection #2 | RS232C extension Unit for Communication #2 (for additional 4 machines : Separately, RS232C cables for communication are required.) |  |
|  | RS232C cable for communication #2 | 5m |  |
|  |  | 10m |  |
|  |  | Optical 30m |  |
|  | Additional RS232C extension unit #2 (Separately, RS232C cables for communication are required.) |  |
| Setup optimizer for multi-PCB production #3 |  |
| Bit-map teaching function #4 |  |
| Mis-programing Check system (Feeder setup error prevention system) (contents : “Software”, one “Bar-cord Reader”, one “IR adaptor station”) |  |
| Additional “Bar-code Reader” |  |
| PC (General communication goods) | (By user) |
| Printer (General commercial goods) | (By user) |

Remark

Only an IBM-PC/AT compatible Windows 98/Me, 2000, NT4.0 (Service Pack 3 or later) installed PC can be adaptable. Other detailed specification should be confirmed by PC manual etc. #1 The Printing function is using Microsoft Internet Explorer 5.0 or later. So, the PC has to be installed it. If the PC has been installed Microsoft Excel 97 or later, the “setup assignment (a kind of YGOS output)” can be output by Excel data files. But, if no, it is output by only CSV data files. So, the PC should be installed for the effectual use. #2 For the RS232C communication, PCI-BUS slots are required. A PCI extension card can communicate with 4 machines. In case of Windows 98/Me, the “Data communication” function can support Max. 128 machines. In case of Windows 2000/ NT4.0, it can support Max. 256 machines (Max. 50 lines). #3 The “setup optimizer” is using Microsoft Excel 97 or later. So, the PC has to be installed it. #4 Separately, a scanner will be needed.

# Software : YVOS X

The “YGOS” is right for a line that contains YAMAHA Xg series mounters exclusively, because of the Library data style (XML format) and LAN communication. In case of the combination with YAMAHA X series mounters and/or YAMAHA hitherto models, the “YVOS X” is easier than the “YGOS” for use.

| Item | Application |
| --- | --- |
| YVOSX basic software (Basic function : offline single unit data optimizing and editing) |  |
| Printing data conversion (VIOS data ( Text printing data) * Printing ability needs “ Microsoft EXCEL 97 “. |  |
| Data conversion ( ASCII data ( VIOS data conversion ) * for other companies machine data and CAD data ( max.128 kind fonts can be set ) |  |
| Line data distribution and optimizing (Setup optimizer for multi-PCB production) |  |
| Communication software (with extension unit, without cables) |  |
| RS232C cable | 5m |  |
|  | 10m |  |
|  | 30m (Optical communication set) |  |
| Extension unit for Communication (for additional 4 units) |  |
| Line control function * including “Line data distribution and optimizing“ and ”Communication software” |  |
| Mis-programming check system (with a “Bar code reader” and an “IR adapter”) (Feeder setting error prevention system) |  |
| Bar cord reader (additional unit) |  |
| Mounting line production control system * Special order : Separately, detail specification sheet will be needed. |  |
| Non-stop production changeover system * Special order : Separately, detail specification sheet will be needed. |  |
| Optima system for feeder exchange carriage (YVOSX expansion program) * Special order : Separately, detail specification sheet will be needed. |  |
| PC (Brand : Model : ) |  |
| Monitor (Brand : Model : ) |  |
| Printer (Brand : Model : ) |  |

An available PC has to be installed “Microsoft Windows95” or “Microsoft Windows98”.

YVOSX needs “Microsoft Internet Explorer”.

Printing ability needs “Microsoft EXCEL 97”.

Communication software needs ISA-bus in the PC.

Communication software cannot be used on “NEC PC98NX PC series”.

Communication software cannot be used on “Microsoft Windows NT”.

Before YVOSX training at YAMAHA or each distributor, please complete the basic training about “Windows95” or “Windows98” by user side.  And, user’s experience of Windows program operation ( for example, EXCEL etc. ) can help the YVOSX training.

# Text boxes

Type203F

1

3

：Area where mounting of components is impossible.

：Area where mounting of components is impossible.

Wmm

Lmm

3mm

3mm

3mm

3mm

Wmm

Ａ

Ｂ

Lmm

C

：Area where mounting of components is impossible.

the locate pin hole and the slot.

C

Previous machine

10.5Ω

２

１

･　･　･　･　･　･　･　･　･　･　･　･　･

13

14

Reset

（N1125）

Max. 25mm

3mm

Max. 6.5mm

[ 4mm ]

3mm

Max. 25mm

3mm

Max. 6.5mm

[ 4mm ]

3mm

L mm

3 mm

W mm

3 mm

Mounting of components is impossible 1mm around

：Area where mounting of components is impossible.

3 mm

W mm

C

L mm

3 mm

Type201F

Type202F

2

Count

+5V

+24V

0.1μ

10.5Ω

（N1120）

Busy　IN

+24V

+5V

（12mm T/F）  （16mm T/F） （24mm T/F）

（32mm T/F）      （44mm T/F）

〇: 8mm T/F installation unavailable position

●: 8mm T/F installation available position

0.1μ

Next machine

This machine

BusyOUT

１

２

･　･　･　･　･　･　･　･　･　･　･　･　･

14

13

(N1831)

＋24V

This machine