# Example Operations Manual Entries for a Company which has a JAR-OPS 3 Dangerous Goods Approval

# SECTION 9	DANGEROUS GOODS AND WEAPONS

Editorial Note 1:	Editorial notes within the following text indicate where the operator needs to add text to describe their specific operation. The editorial notes must be replaced with the operator’s own text before submission to the CAA.

Editorial Note 2:	The following text makes numerous references to the International Civil Aviation Organization’s Technical Instructions for the Safe Transport of Dangerous Goods by Air (Technical Instructions). Should the Operator have decided to use the IATA Dangerous Goods Regulations in lieu of the ICAO Technical Instructions, references to the ICAO Technical Instructions should be amended accordingly.

## 9.1 	Policy on the Transport of Dangerous Goods

### 9.1.1	Approval for the Transport of Dangerous Goods (JAR-OPS 3.1155, IEM 3.1155)

Dangerous goods can only be carried according to the International Civil Aviation Organization's Technical Instructions for the Safe Transport of Dangerous Goods by Air (Technical Instructions), irrespective of whether the flight is wholly or partly within or wholly outside the territory of a State. An approval must be granted by the State of the Operator before dangerous goods can be carried on an aircraft, except as identified in 9.1.3 and 9.1.5 below. An additional approval or an exemption may be required to permit the transport of some dangerous goods - see 9.1.2 below.

Editorial Note 1:	Insert Text [Operator Name] holds approval for the transport of dangerous goods by air in accordance with JAR-OPS 3.1155.

Editorial Note 2:	Should the Operator’s policy prohibit the carriage of certain dangerous goods (e.g. radioactive material) these restrictions should be stated.

Editorial Note 3:	Insert Text The following [person or post holder] is assigned responsibility for the Approval held:

[Job Title/Name and contact details]

Editorial Note 4: As queries regarding the carriage of dangerous goods will often be escalated to the nominated person, arrangements need to be established to ensure continuity of supervision in the absence of the person nominated by the operator as having overall responsibility for the transport of dangerous goods by air.

### 9.1.2	Forbidden Dangerous Goods (JAR-OPS 3.1165(a))

Certain dangerous goods, which are normally forbidden, may be specifically approved for air transport by the State of Origin and the State of the Operator:

- to transport dangerous goods forbidden on passenger and/or cargo aircraft 		where Special Provision A1/A2 applies; or

- for other purposes as specified in the ICAO Technical Instructions;

provided that in such instances an overall level of safety in transport which is at least equivalent to the level of safety provided for in these Instructions is achieved.

In instances of extreme urgency or when other forms of transport are inappropriate or full compliance with the prescribed requirements is contrary to public interest, the States concerned may grant an exemption from the provisions of the Instructions provided that in such instances an overall level of safety in transport which is at least equivalent to the level of safety provided for in these Instructions is achieved. For the purposes of exemptions, “States concerned” are the States of Origin, Operator, transit, overflight and destination. For the State of overflight, if none of the criteria for granting an exemption are relevant, an exemption may be granted based solely on whether it is believed that an equivalent level of safety in air transport has been achieved. Additionally, since controls exist for the quantities of some explosives which may be carried to or from specific airfields in the United Kingdom, operators must seek advice from the Civil Aviation Authority as to the suitability of the intended airfield of loading and unloading when Class 1 dangerous goods are being carried under an A2 approval.

Note: 	Application for approvals should be submitted to the CAA Dangerous Goods Office at least 10 working days prior to the proposed flight date.

Dangerous goods carried in accordance with an exemption or approval must comply with the conditions on the exemption or approval, as well as those on the permanent approval unless these have been varied by the exemption or further approval.

Editorial Note 1: The operator’s procedure for ensuring relevant personnel are made aware of the details of short-term approvals and exemptions regarding the dangerous goods (e.g. through the issue of crew notices) should be described.

Editorial Note 2: Operators holding specific non-expiring approvals or exemptions related to the carriage of dangerous goods should provide details of these and the conditions of carriage specified therein.

### 9.1.3	General Exceptions

#### 9.1.3.1	Airworthiness and Operational Items (JAR-OPS 3.1160(b)(1) and (2))

An approval is not required for dangerous goods which are required to be aboard the aircraft as:

a)	items for airworthiness or operating reasons or for the health of passengers or crew,  such as batteries, fire extinguishers, first-aid kits, insecticides, air fresheners, life rafts, escape slides, life-saving appliances, portable oxygen supplies, tritium signs, smoke hoods, passenger service units; and

- catering or cabin service supplies; and

- electronic devices such as electronic flight bags, personal entertainment devices, credit card readers, containing lithium metal or lithium ion cells or batteries and spare lithium batteries for such devices carried aboard an aircraft by the operator for use on the aircraft during the flight or series of flights, provided that the batteries meet the provisions applicable to the carriage of portable electronic devices containing lithium or lithium ion cells or batteries by passengers (see the entry for ‘consumer articles’ in the table produced at 9.1.5).  Spare lithium batteries must be individually protected so as to prevent short circuits when not in use. Conditions for the carriage and use of these electronic devices and for the carriage of spare batteries must be provided in the operations manual and/or other appropriate manuals as will enable flight crew, cabin crew and other employees to carry out their responsibilities.

Note:	Dangerous goods intended as replacements for those referred to in 9.1.3.1 a and b above may not be carried without the approval referred to in 9.1.1 and unless consigned and accepted for transport in accordance with the ICAO Technical Instructions.

#### 9.1.3.2	Veterinary Aid (JAR-OPS 3.1160(b)(3))

An approval is not required for dangerous goods which are carried for use in flight as veterinary aid or as a humane killer for an animal. Such dangerous goods must be stowed and secured during take-off and landing and at all other times when deemed necessary by the pilot-in-command. The dangerous goods must be under the control of trained personnel during the time when they are in use on the aircraft.

Dangerous goods may be carried on a flight made by the same aircraft before or after a flight for which they are required as veterinary aid or as a humane killer for an animal, when it is impracticable to load or unload the dangerous goods immediately before or after the flight, subject to the following conditions:

a)	the dangerous goods must be capable of withstanding the normal conditions of air transport;

b)	the dangerous goods must be appropriately identified (e.g. by marking or labelling);

c)	the dangerous goods may only be carried with the approval of the operator;

d)	the dangerous goods must be inspected for damage or leakage prior to loading;

e)	loading must be supervised by the operator;

f)	the dangerous goods must be stowed and secured in the aircraft in a manner that will prevent any movement in flight which would change their orientation;

g)	the pilot-in-command must be notified of the dangerous goods loaded on board the aircraft and their loading location. In the event of a crew change, this information must be passed to the next crew;

h)	all personnel must be trained commensurate with their responsibilities; and

i)	the provisions of 11.10.4 (Dangerous Goods Accident and Incident Reports) apply.

#### 9.1.3.3	Medical Aid for a Patient (JAR-OPS 3.1160(b)(4))

An approval is not required for dangerous goods which:

a)	are placed on board an aircraft with the approval of the operator; or

b)	form part of the permanent equipment of the aircraft when it has been adapted for specialised use,

to provide, during flight, medical aid for a patient, such as gas cylinders, drugs, medicines, other medical material (e.g. sterilising wipes) and wet cell or lithium batteries, providing:

i)	the gas cylinders have been manufactured specifically for the purpose of containing and transporting that particular gas;

ii)	the drugs and medicines and other medical matter are under the control of trained personnel during the time when they are in use;

iii)	the equipment containing wet cell batteries is kept, and when necessary secured, in an upright position to prevent spillage of the electrolyte; and

iv)	proper provision is made to stow and secure all the equipment during take-off and landing and at all other times when deemed necessary by the commander in the interests of safety.

These dangerous goods may also be carried on a flight made by the same aircraft to collect a patient or after that patient has been delivered when it is impracticable to load or unload the goods at the time of the flight on which the patient is carried.

Note:	The dangerous goods carried may differ from those identified above due to the needs of the patient. These provisions apply both to dedicated air ambulances and to temporarily modified aircraft.

#### 9.1.3.4	Excess baggage being sent as cargo

An approval is not required for dangerous goods contained within items of excess baggage being sent as cargo provided that:

- the excess baggage has been consigned as cargo by or on behalf of a passenger;

- the dangerous goods may only be those that are permitted by and in accordance with 9.1.5 to be carried in checked baggage; and

- the excess baggage is marked with the words “Excess baggage consigned as cargo”.

### 9.1.4	Instructions on the Carriage of Employees of the Operator (JAR-OPS 3.1210)

There is no restriction of the carriage of employees on an aircraft carrying dangerous goods which are permitted on a passenger aircraft, providing the requirements of the Technical Instructions are complied with. When an aircraft is carrying dangerous goods which can only be carried on a cargo aircraft, employees of the operator can also be carried provided they are in an official capacity. It is intended this be interpreted as meaning they have duties concerned with the preparation or undertaking of a flight or on the ground once the aircraft has landed, although not necessarily in connection with an aircraft. See also 9.3.4.

### 9.1.5	Items That May Be Carried by Passengers and Crew (JAR-OPS 3.1160(b)(5))

Editorial Note 1: International standards permit the carriage of the dangerous goods listed below by passengers or crew members either as or in carry-on baggage or checked baggage or on their person. Additional restrictions implemented by countries in the interests of aviation security may, however, limit or forbid the carriage of some of these items.

Editorial Note 2: Certain items listed are permitted only with the operator’s approval. Requirements apply to some items regarding the means by which they are prepared for transport (e.g. wheelchairs and battery-powered mobility devices) or the professional status of the passenger (e.g. Chemical Agent Monitoring Equipment). The operator’s policy towards the carriage of items listed as requiring operator’s approval should be established. This should include details of how passengers are expected to declare their intention to carry an item, how its proper preparation will be confirmed and how details will be passed to ground handlers (as required). If case-by-case consideration is considered appropriate for items requiring operator approval, the person or role within the operation that may grant approval for the carriage of such items and the basis upon which approvals will be granted should be stated.

An approval is not required for those dangerous goods which, according to the Technical Instructions, can be carried by passengers or crew members as per the following table:

Note:	Should it be necessary to transfer carry-on baggage to the hold (e.g. due to the size of the baggage preventing proper stowage in the cabin) it is necessary for cabin crew to verify that the baggage contains no dangerous goods that are permitted for carriage in carry-on baggage only (e.g. spare lithium batteries, heat producing articles etc).

| Medical Necessities | Carry-on baggage | Checked (hold) baggage | On one’s person | Operator approval required |
| --- | --- | --- | --- | --- |
| Gaseous oxygen or air cylinders required for medical use. Each cylinder must not exceed 5 kg gross mass. Cylinders, valves and regulators, where fitted, must be protected from damage which could cause inadvertent release of the contents. The pilot-in-command must be informed of the number of oxygen or air cylinders loaded on board the aircraft and their loading location(s). Note 1: Liquid oxygen systems are forbidden. Note 2: Air cylinders for other purposes, such as scuba diving, may only be carried if “empty”. |  |  |  |  |
| Cylinders of a non-flammable, non-toxic gas, worn for the operation of mechanical limbs, also spare cylinders of a similar size if required to ensure an adequate supply for the duration of the journey. |  |  |  |  |
| Non-radioactive medicines (including aerosols). The total net quantity of each single article must not exceed 0.5 kg or 0.5 L. Release valves on aerosols must be protected by a cap or other suitable means to prevent inadvertent release of the contents. Note: The total net quantity of medicines, toiletry articles and aerosols for sporting or home use must not exceed 2 kg or 2 L (e.g. four aerosol cans of 500 mL each) for each person. |  |  |  |  |
| Small medical or clinical thermometer which contains mercury, one only, for personal use when in its protective case. |  |  |  |  |
| Radioisotopic cardiac pacemakers or other devices, including those powered by lithium batteries, implanted into a person, or radio-pharmaceuticals contained within the body of a person as the result of medical treatment. |  |  |  |  |
| Wheelchairs or other battery-powered mobility aids with non-spillable batteries, which comply with Special Provision A67 or the vibration and pressure differential tests of Packing Instruction 872, for use by passengers whose mobility is restricted by either a disability, their health or age, or a temporary mobility problem (e.g. broken leg). The battery must be securely attached to the wheelchair. The wheelchair battery and its controls must be protected from: a) inadvertent operation - there are a variety of ways a wheelchair can be protected, and in the first instance the passenger should be asked how this can be achieved; generally this will involve certain actions being taken with the joystick, but may also be as simple as removing a key or turning a deactivation switch. If the latter, care must be taken during loading to ensure that the switch cannot be activated by adjacent baggage. Note: Application of the brake is not sufficient; unless the motor is rendered inoperative the motor can still be activated and overheat; b) short circuit of the battery – this does not necessarily require disconnection, since this is often very difficult to do, and if not done properly can increase the risk of a fire. Adequate protection may already be afforded by the battery being contained in a battery box fitted to the mobility aid. Consequently, only if deactivation cannot be achieved should disconnection be considered, following which it must be ensured that the battery terminals are protected against short circuit, e.g. by the effective insulation of exposed terminals; and c) damage – including to associated wiring, by the movement of baggage, mail, stores or other cargo. |  |  | N/A |  |
| Wheelchairs or other battery-powered mobility aids with spillable batteries, for use by passengers whose mobility is restricted by either a disability, their health or age, or a temporary mobility problem (e.g. broken leg), provided that the wheelchair or mobility aid can be loaded, stowed, secured and unloaded always in an upright position and that the battery terminals are protected from short circuits (e.g. by being enclosed within a battery container) and the battery is securely attached to the wheelchair or mobility aid. The operator must ensure that wheelchairs or other battery-powered mobility aids are carried in such a manner so as to prevent unintentional activation and that they are protected from being damaged by the movement of baggage, mail, stores or other cargo. Note: If the wheelchair or mobility aid cannot be loaded, stowed, secured and unloaded always in an upright position (which will depend upon the type of aircraft and the type of the mobility aid), the battery must be removed and the wheelchair or mobility aid may then be carried as checked baggage without restriction. A removed spillable battery may only be carried by air if packed, marked and labelled as specified within the ICAO Technical Instructions. |  |  | N/A |  |
| Lithium-ion battery-powered wheelchairs or other similar mobility aids for use by passengers whose mobility is restricted by either a disability, their health or age, or a temporary mobility problem (e.g. broken leg), subject to the following conditions: 1) the batteries must be of a type which meets the requirements of each test in the UN Manual of Tests and Criteria, Part III, section 38.3; 2) battery terminals must be protected from short circuits (e.g. by being enclosed within a battery container) and should be securely attached to the mobility aid; 3) the operator(s) must ensure that such mobility aids are carried in a manner so as to prevent unintentional activation and that they are protected from being damaged by the movement of baggage, mail, stores or other cargo; and 4) the pilot-in-command must be informed of the location of the mobility aid. |  |  | N/A |  |
| Portable medical electronic devices (Automated External Defibrillators (AED), Nebulizer, Continuous Positive Airway Pressure (CPAP), etc.) containing lithium metal or lithium ion cells or batteries carried by passengers for medical use. No more than two spare batteries may be carried. Spare batteries must be individually protected so as to prevent short circuits (by placement in original retail packaging or by otherwise insulating terminals, e.g. by taping over exposed terminals or placing each battery in a separate plastic bag or protective pouch). Each installed or spare battery must be of a type which meets the requirements of each test in the UN Manual of Tests and Criteria, Part III, section 38.3; In addition, each installed or spare battery must not exceed the following: i) for lithium metal batteries, a lithium content of not more than 8 grams; or ii) for lithium ion batteries, a watt-hour rating of not more than 160 Wh. NOTE: Spare batteries may be carried in carry-on baggage only. |  | See Note |  |  |

| Articles Used in Dressing or Grooming | Carry-on baggage | Checked (hold) baggage | On one’s person | Operator approval required |
| --- | --- | --- | --- | --- |
| Toiletry articles (including aerosols). The total net quantity of each single article must not exceed 0.5 kg or 0.5 L. Release valves on aerosols must be protected by a cap or other suitable means to prevent inadvertent release of the contents. The term “toiletry articles (including aerosols)” is intended to include such items as hair sprays, perfumes and colognes. Note: The total net quantity of medicines, toiletry articles and aerosols for sporting or home use must not exceed 2 kg or 2 L (e.g. four aerosol cans of 500 mL each) for each person. |  |  |  |  |
| Hair curlers containing hydrocarbon gas, no more than one per person, provided that the safety cover is securely fitted over the heating element. Note: Gas refills for such curlers must not be carried. |  |  |  |  |

| Consumer Articles | Carry-on baggage | Checked (hold) baggage | On one’s person | Operator approval required |
| --- | --- | --- | --- | --- |
| Alcoholic beverages, containing more than 24% but not more than 70% alcohol by volume, when in retail packagings in receptacles not exceeding 5 L, with a maximum total net quantity per person of 5 L for such beverages. Note: Alcoholic beverages containing not more than 24% alcohol by volume are not subject to any restrictions. Alcoholic beverages with more than 70% alcohol by volume are not permitted. |  |  |  |  |
| Aerosols (non-flammable, non-toxic) with no subsidiary risk, for sporting or home use. Permitted in checked baggage only. The total net quantity of each single article must not exceed 0.5 kg or 0.5 L. Release valves on aerosols must be protected by a cap or other suitable means to prevent inadvertent release of the contents. Note: The total net quantity of medicines, toiletry articles and aerosols for sporting or home use must not exceed 2 kg or 2 L (e.g. four aerosol cans of 500 mL each) for each person. |  |  |  |  |
| Ammunition (cartridges for weapons) securely packed in quantities not exceeding 5 kg gross mass per person for that person’s own use. Allowances for more than one person must not be combined into one or more packages. Note: Only ammunition classified as UN0012 or UN0014 within Division 1.4S may be carried in baggage. If the classification is unknown, this information should be obtained from the ammunition manufacturer/supplier. |  |  |  |  |
| One small packet of safety matches or a single cigarette lighter (that does not contain unabsorbed liquid fuel, other than liquefied gas), intended for use by an individual. Note 1: Lighter fuel and lighter refills are not permitted on one’s person or in checked or carry-on luggage. Note 2: ‘Strike anywhere’ matches are forbidden for air transport. |  |  |  |  |
| Portable electronic devices containing lithium or lithium ion cells or batteries (watches, calculating machines, cameras, cellular phones, laptop computers, camcorders, etc.) when carried by passengers or crew for personal use. Each installed or spare battery must not exceed the following: - for lithium metal batteries, a lithium content of not more than 2 grams; or - for lithium ion batteries, a watt-hour rating of not more than 100 Wh. Note: Carriage should be as carry-on baggage. |  | See Note | See Note |  |
| Spare lithium or lithium ion cells or batteries must be individually protected so as to prevent short circuits (by placement in original retail packaging or by otherwise insulating terminals, e.g. by taping over exposed terminals or placing each battery in a separate plastic bag or protective pouch) and carried in carry-on baggage only. Each spare battery must not exceed the following: - for lithium metal or lithium alloy batteries, a lithium content of not more than 2 grams; or - for lithium ion batteries, a watt-hour rating of not more than 100 Wh. |  |  |  |  |
| Portable electronic devices containing lithium ion batteries exceeding a watt-hour rating of 100 Wh but not exceeding 160 Wh in equipment may be carried in either checked or carry-on baggage. |  |  |  |  |
| Spare lithium ion batteries exceeding a watt-hour rating of 100 Wh but not exceeding 160 Wh may be carried in carry-on baggage. Each lithium ion cell or battery must be individually protected so as to prevent short circuits (by placement in original retail packaging or by otherwise insulating terminals, e.g. by taping over exposed terminals or placing each battery in a separate plastic bag or protective pouch). No more than two individually protected spare batteries per person may be carried. |  |  |  |  |
| Portable electronic devices powered by fuel cells and up to two spare fuel cell cartridges (cameras, mobile phones, laptop computers, camcorders, etc). Fuel cells and fuel cell cartridges may only contain flammable liquids, corrosive substances, liquefied flammable gas, water reactive substances or hydrogen in metal hydride. Refuelling of fuel cells on board an aircraft is not permitted except that the installation of a spare cartridge is allowed. Note: SPECIFIC TECHNICAL SPECIFICATIONS APPLY – SEE BELOW. |  |  |  |  |
| Self-inflating life-jacket fitted with no more than two small cylinders containing a non-toxic, non-flammable gas, and no more than two spare cylinders. |  |  |  |  |
| Avalanche rescue backpack equipped with a pyrotechnic trigger mechanism containing not more than 200 mg net of Division 1.4S and a cylinder of compressed non-toxic, non-flammable gas not exceeding 250 ml. One per person permitted. Note: The backpack must be packed in such a manner that it cannot be accidentally activated. The airbags within the backpack must be fitted with pressure relief valves. |  |  |  |  |
| Dry ice in quantities not exceeding 2.5 kg per person, when used to pack perishables that are not dangerous goods, provided the package permits the release of carbon dioxide gas. When carried in checked baggage, each package must be marked ‘DRY ICE’ or ‘CARBON DIOXIDE, SOLID’ and with the net weight of dry ice or an indication that the net weight is 2.5 kg or less. |  |  |  |  |
| Mercurial barometer or mercurial thermometer carried by a representative of a government weather bureau or similar official agency. The barometer or thermometer must be packed in a strong outer packaging, having a sealed inner liner or a bag of strong leak-proof and puncture-resistant material impervious to mercury, which will prevent the escape of mercury from the package irrespective of its position. |  |  |  |  |
| Battery-powered equipment capable of generating extreme heat, which could cause a fire if activated (e.g. underwater high intensity lamps) providing that the heat-producing component or the battery is packed separately so as to prevent activation during transport. Any battery which has been removed must be protected against short circuit. |  |  |  |  |
| Instruments containing radioactive material not exceeding the activity limits specified in Table 2-12 of the ICAO Technical Instructions (i.e. chemical agent monitor (CAM) and/or rapid alarm and identification device monitor (RAID-M)), securely packed and without lithium batteries, when carried by staff members of the Organization for the Prohibition of Chemical Weapons (OPCW) on official travel. |  |  |  |  |
| Energy efficient light bulbs when in retail packaging intended for personal or home use. |  |  |  |  |

| Security Type Equipment | Carry-on baggage | Checked (hold) baggage | On one’s person | Operator approval required |
| --- | --- | --- | --- | --- |
| Security type equipment such as attaché cases, cash boxes, cash bags, etc. incorporating dangerous goods as part of this equipment, for example lithium batteries or pyrotechnic material, only if the equipment complies with the technical specification below. |  |  |  |  |

##### Additional Technical Specifications:

FUEL CELL CARTRIDGES – TECHNICAL SPECIFICATION

Fuel cells must meet the following specification:

1)	fuel cells and fuel cell cartridges may only contain flammable liquids, corrosive substances, liquefied flammable gas, water reactive substances or hydrogen in metal hydride;

2)	refuelling of fuel cells on board and aircraft is not permitted except that the installation of a spare cartridge is allowed;

3)	the maximum quantity of fuel in any fuel cell or fuel cell cartridge must not exceed:

a)	for liquids 200 mL;

b)	for solids 200 grams;

c)	for liquefied gases, 120 mL for non-metallic fuel cells or fuel cell cartridges or 200 mL for metal fuel cells or fuel cell cartridges; and

d)	for hydrogen in metal hydride, the fuel cell cartridges must have a water capacity of 120 mL or less;

4)	each fuel cell and each fuel cell cartridge must conform to IEC PAS 62282-6-1 Ed. 1, and must be marked with a manufacturer’s certification that it conforms to the specification. In addition, each fuel cell cartridge must be marked with the maximum quantity and type of fuel in the cartridge;

5)	fuel cell cartridges containing hydrogen in metal hydride must comply with the requirements in Special Provision A162;6)	no more than two spare fuel cell cartridges may be carried by a passenger as follows:

a) fuel cell cartridges containing flammable liquids, corrosive substances, liquefied flammable gas or hydrogen in metal hydride in carry-on baggage, in checked baggage or on the person; and

b) fuel cell cartridges containing water-reactive substances in carry-on baggage or on the person;

7)	fuel cells containing fuel are permitted in carry-on baggage only;

8)	interaction between fuel cells and integrated batteries in a device must conform to IEC PAS 62282-6-1 Ed. 1. Fuel cells whose sole function is to charge a battery in the device are not permitted;

9)	fuel cells must be of a type that will not charge batteries when the portable electronic device is not in use and must be durably marked by the manufacturer: “APPROVED FOR CARRIAGE IN AIRCRAFT CABIN ONLY” to so indicate; and

10)	in addition to the languages which may be required by the State of Origin for the markings specified above, English should be used.

SECURITY TYPE EQUIPMENT –TECHNICAL SPECIFICATION

1) 	the equipment must be equipped with an effective means of preventing accidental activation;

2) 	if the equipment contains an explosive or pyrotechnic substance or an explosive article, this article or substance must be excluded from Class 1 by the appropriate national authority of the State of Manufacture in compliance with Part 2;1.5.2.1 of the ICAO Technical Instructions;

3) 	if the equipment contains lithium cells or batteries, these cells or batteries must comply with the following restrictions:

a) 	for a lithium metal cell, the lithium content is not more than 1 g;

b) 	for a lithium metal or lithium alloy battery, the aggregate lithium content is not more than 2 g;

c) 	for lithium ion cells, the Watt-hour rating is not more than 20 Wh;

d) 	for lithium ion batteries, the Watt-hour rating is not more than 100 Wh;

e) 	each cell or battery is of the type proven to meet the requirements of each test in the UN Manual of Tests and Criteria, Part III, section 38.3;

4) 	if the equipment contains gases to expel dye or ink, only gas cartridges and receptacles, small, containing gas with a capacity not exceeding 50 mL, containing no constituents subject to these Instructions other than a Division 2.2 gas, are allowed. The release of gas must not cause extreme annoyance or discomfort to crew members so as to prevent the correct performance of assigned duties. In case of accidental activation, all hazardous effects must be confined within the equipment and must not produce extreme noise.

5) 	security type equipment that is defective or that has been damaged is forbidden for transport.

NOTE: 	Security type equipment not meeting the above technical specification is forbidden for carriage in any circumstances.

### 9.1.6	Provision of Information to Passengers (JAR-OPS 3.1215(b)(1))

Editorial Note: An operator must ensure that information on the types of dangerous goods which a passenger is forbidden to transport aboard an aircraft is provided at the point of ticket purchase. Information provided via the Internet may be in text or pictorial form but should be such that ticket purchase cannot be completed until the passenger, or a person acting on their behalf, has indicated that they have understood the restrictions on dangerous goods in baggage.

An operator or the operator’s handling agent and the airport operator must ensure that notices warning passengers of the types of dangerous goods which they are forbidden to transport aboard an aircraft are prominently displayed, in sufficient number, at each of the places at an airport where tickets are issued, passengers are checked in and aircraft boarding areas are maintained, and at any other location where passengers are checked in. These notices must include visual examples of dangerous goods forbidden from transport aboard an aircraft.

An operator, of passenger aircraft, should have information on those dangerous goods which may be carried by passengers made available prior to the check-in process on their websites or other sources of information.

The provisions above with respect to ticket purchase on operator websites will become mandatory in the 2013-2014 Edition of the ICAO Technical Instructions.

Operators should describe the means of promulgating such information to passengers.

### 9.1.7	Marking and Labelling of Packages

Articles and substances meeting the dangerous goods classification criteria are assigned a ‘UN Number’ under the United Nations classification system.  This consists a four-digit number preceded by the capital letters ‘UN’.  Packages of dangerous goods must be marked with the UN Number(s) applicable to their contents.

Packages containing dangerous goods can also be identified by labels indicating the hazard of the goods by their class or division or by the presence of certain handling labels/markings.

Note:	When dangerous goods markings or labels are seen on items not declared as dangerous goods it is often an indication that they do contain such goods. Undeclared dangerous goods must not be loaded on an aircraft and reporting procedures must be implemented (see 11.10.4).

| CLASS 1 – EXPLOSIVE |
| --- |
| Class 1 (with exploding bomb symbol) - explosives generally not permitted on an aircraft. * Division and compatibility group | Class 1 (without exploding bomb symbol) - explosives usually permitted on an aircraft. ** Compatibility group |

| CLASS 2 – GASES |
| --- |
| Flammable gas (Division 2.1) | Non-flammable, non-toxic gas (Division 2.2) | Toxic gas (Division 2.3) |

CLASS 3 – FLAMMABLE LIQUID

| CLASS 4 – FLAMMABLE SOLIDS |
| --- |
| Flammable solid (Division 4.1) | Substance liable to spontaneous combustion (Division 4.2) | Substance which, in contact with water, emits flammable gas (Division 4.3) |

| CLASS 5 – OXIDISING SUBSTANCES AND ORGANIC PEROXIDES |
| --- |
| Oxidising substance (Division 5.1) | Organic peroxide (Division 5.2) (flame may be black or white) |

| CLASS 6 – TOXIC AND INFECTIOUS SUBSTANCES |
| --- |
| Toxic substance (Division 6.1) | Infectious substance (Division 6.2) |
|  |  | The bottom part of the label should bear the inscription: “INFECTIOUS SUBSTANCE — In case of damage or leakage immediately notify public health authority”. |

| CLASS 7 – RADIOACTIVE MATERIAL |
| --- |
| Category I | Category II | Category III |
| Criticality safety index label |  |
| CLASS 8 – CORROSIVE |

CLASS 9 – MISCELLANEOUS

| HANDLING LABELS |
| --- |
| Packages of dangerous goods may also bear labels providing handling information; these are: |
| Magnetized material | Cargo aircraft only |
| Cryogenic liquid label | Package orientation (red or black) | Keep away from heat |

Intermediate Bulk Containers (IBCs) are only permitted for the transport of UN 3077 Environmentally hazardous substance, solid, n.o.s.  The maximum permitted stacking load applicable when the IBC is in use must be displayed on a symbol as follows:

| IBCs capable of being stacked | IBCs NOT capable of being stacked |
| --- | --- |

| Lithium Battery Handling Label | Application of the lithium battery handling label to a consignment of lithium batteries (of any type) indicates that the Shipper has determined specific requirements have been met. Such consignments do not need to be accompanied by a dangerous goods transport document (Shipper’s Declaration) and no acceptance check is required. Consignments bearing the lithium battery label must be accompanied with a document such as an air waybill with: — an indication that the package contains lithium metal cells or batteries; — an indication that the package must be handled with care and that a flammability hazard exists if the package is damaged; — an indication that special procedures should be followed in the event the package is damaged, to include inspection and repacking if necessary; — a telephone number for additional information; and — When an air waybill is issued the applicable Packing Instruction must be stated together with the words ‘not restricted’; and ‘lithium ion batteries’ or ‘lithium metal batteries’ as applicable. |
| --- | --- |

| EXCEPTED QUANTITIES MARKING |
| --- |
| Packages containing excepted quantities of dangerous goods can be identified from the following |
|  | Hatching and symbol of the same colour, black or red, on white or suitable contrasting background. * Place for class or, when assigned, the division number(s). ** Place for name of shipper or consignee, if not shown elsewhere on the package. |

| LIMITED QUANTITIES MARKING |
| --- |
| Packages containing limited quantities of dangerous goods can be identified from the following: |
|  | Many dangerous goods when in reasonably limited quantities present a reduced hazard during transport and can safely be carried in good quality packagings that have not been tested and marked as is required for UN Specification packagings required for larger quantities of dangerous goods. Packages containing limited quantities of dangerous goods must be marked with a diamond shaped mark. When presented for carriage by air, the mark must additionally include a “Y” which indicates compliance with the provisions of the ICAO Technical Instructions, some of which are more stringent than those of the UN Model Regulations and of other modes of transport. NOTE: The marking depicted here but without the ‘Y’ indicates that the package contains dangerous goods in limited quantities as permitted by surface transport regulations (ADR/IMDG) which may not be acceptable for air transport. A package so marked and offered for transport in the absence of a dangerous goods transport document must be reported to the appropriate authority where the goods are discovered as a discovery of undeclared dangerous goods (the CAA if discovered within the UK). |

| ENVIRONMENTALLY HAZARDOUS SUBSTANCES MARKING |
| --- |
|  | Packages containing environmentally hazardous substances (UN Nos. 3077 and 3082) must be durably marked with the environmentally hazardous substance mark with the exception of single packagings and combination packagings containing inner packagings with contents of 5 L or less for liquids; or contents of 5 kg or less for solids. ALL packages containing environmentally hazardous substances must bear a Class 9 hazard label. |

## 9.2	Duties of All Personnel Involved

### 9.2.1	Detailed Assignments of Responsibilities (JAR-OPS 3.1215(a))

Editorial Note 1: Operators need to assign the key responsibilities associated with the carriage of dangerous goods. For example, it may be intended for acceptance checks of consignments of dangerous goods cargo to be conducted by suitably trained ground staff of the operator or alternatively by a designated handling agent. Duties associated with the carriage of dangerous goods include:

| Person Nominated as Responsible for Operator’s Dangerous goods Approval | Oversight and control of the carriage of dangerous goods. Ensuring all necessary permissions, approvals and exemptions are held. Generation (or acceptance) of relevant procedures. Responding to queries regarding the carriage of dangerous goods. |
| --- | --- |
| Cargo Department/ Cargo Sales Agents | Arrangement of the carriage of dangerous goods only in accordance with the operator’s stated policies. Recognition of undeclared dangerous goods. |
| Persons receiving or handling general cargo, mail and stores | Recognition of undeclared dangerous goods. Dealing with dangerous goods that are found damaged or leaking during processing for transport. If there is a dangerous goods incident or accident, or if undeclared dangerous goods are detected, a report is made to the appropriate Authority (see 11.10.4). |
| Persons receiving or handling dangerous goods | Acceptance procedures for dangerous goods are carried out as required by the Technical Instructions. Inspection procedures during the processing of dangerous goods for transport are carried out as required by the Technical Instructions. Dealing with dangerous goods that are found damaged or leaking during processing for transport. Dangerous goods are loaded, segregated, stowed and secured on an aircraft in accordance with the Technical Instructions. Generation of written information to the commander (NOTOC). Provision of written information about dangerous goods loaded on board to the commander for signature. Retention of documentation on the ground. Recognition of undeclared dangerous goods. If there is a dangerous goods incident or accident, or if undeclared dangerous goods are detected, a report is made to the appropriate Authority (see 11.10.4). |
| Reservations | Ensuring that information is provided with the passenger ticket or in another manner such that prior to or during the check-in process the passenger receives the information. Considering passenger requests for approval of the operator for items of dangerous goods requiring such approval. |
| Persons handling passengers | Ensuring that the provisions concerning passengers and dangerous goods are complied with. Ensuring that notices are displayed in sufficient number and prominence at each of the places at an airport where tickets are issued, passengers checked in and aircraft boarding areas maintained, and at any other location where passengers are checked in. With the aim of preventing dangerous goods which passengers are not permitted to have from being taken on board an aircraft in their baggage, seeking confirmation from a passenger about the contents of any item where there are suspicions that it may contain dangerous goods. Ensuring that the discovery of prohibited dangerous goods (after a passenger has checked in) is reported to the appropriate Authority (see 11.10.4). |
| Cabin Crew | Ensuring that the provisions concerning passengers and dangerous goods are complied with. Responding to a dangerous goods incident or accident in the cabin. Ensuring that a dangerous goods incident or accident in the cabin, or the discovery of prohibited dangerous goods (after a passenger has boarded), is reported to the appropriate Authority (see 11.10.4). |
| Operations Personnel | If there is an aircraft incident or accident, information is passed to emergency services and state Authorities as required by the Technical Instructions (see 11.10.2). If there is a dangerous goods incident or accident, or if undeclared dangerous goods are detected, a report is made to the appropriate Authority (see 11.10.4). |
| Flight Crew | Signature of NOTOC to indicate receipt of information. If an in-flight emergency occurs, as soon as the situation permits, passage of details of dangerous goods on board to the appropriate Air Traffic Services Unit. |
| Trainers | Provision of initial and recurrent dangerous goods training commensurate with the responsibilities of the personnel concerned. |
| Quality Auditors | Establishment and operation of the Quality System to monitor compliance with procedures for dangerous goods, provision of dangerous goods training, etc. Collation and assessment of details of dangerous goods incidents, accidents and the discovery of undeclared dangerous goods within the accident prevention and flight safety programme. |

Editorial Note 2: In practice a ground handling agent may carry out some or all of the procedures for processing dangerous goods cargo for air transport. A ground handling agent must be provided with sufficient information to enable these procedures to be actioned. Operators should specify whether they utilise suitably qualified personnel of the operator or of a handling agent at the various aerodromes of the operation.

## 9.3	Guidance on the Requirements for Acceptance, Handling and Stowage (JAR-OPS 3.1195, 3.1200, 3.1210)

9.3.1	Acceptance Check

An operator must not accept for transport aboard an aircraft a package or overpack containing dangerous goods or a freight container containing radioactive material or a unit load device or other type of pallet containing dangerous goods as cargo unless the operator has, by use of a checklist, verified the following:

a)	the documentation or, when provided, the electronic data is compliant with the applicable requirements;

b)	the quantity of dangerous goods stated on the dangerous goods transport document is within the limits per package on a passenger or cargo aircraft as appropriate;

c)	the marking of the package, overpack or freight container accords with the details stated on the accompanying dangerous goods transport document and is clearly visible;

d)	where required, the letter in the packaging specification marking designating the packing group for which the design type has been successfully tested is appropriate for the dangerous goods contained within. This does not apply to overpacks where the specification marking is not visible;

e)	proper shipping names, UN numbers, labels, and special handling instructions appearing on the interior package(s) are clearly visible or reproduced on the outside of an overpack;

f)	the labelling of the package, overpack or freight container is as required for the consignment;

g)	the outer packaging of a package is of the type stated on the accompanying dangerous goods transport document and is permitted by the applicable packing instruction;

h)	the package or overpack does not contain different dangerous goods which require segregation from each other;

i)	the package, overpack, freight container or unit load device is not leaking and there is no indication that its integrity has been compromised; and

j)	an overpack does not contain packages bearing the “Cargo aircraft only” label unless:

1)	the packages are assembled in such a way that clear visibility and easy access to them is possible; or

2)	the packages are not required to be accessible; or

3)	not more than one package is involved.

Note 1:	An acceptance check is not required for dangerous goods in excepted quantities, radioactive material in excepted packages and lithium batteries consigned in accordance with Section II of the applicable packing instruction..

Note 2:	Persons conducting dangerous goods acceptance checks must have received dangerous goods training commensurate with this responsibility. Acceptance checks conducted in the United Kingdom must only be conducted by a person who has successfully completed training applicable to this role from a CAA Approved Dangerous Goods Training Organisation.

9.3.2	Inspections for Damage or Leakage

A package or overpack containing dangerous goods must not be loaded onto an aircraft or into a unit load device unless it has been inspected immediately prior to loading and found free from evidence of leakage or damage. A unit load device must not be loaded aboard an aircraft unless the device has been inspected and found free from any evidence of leakage from or damage to any dangerous goods contained therein.  Packages or overpacks containing dangerous goods must be inspected for signs of damage or leakage upon unloading from the aircraft or unit load device.

9.3.3	Prohibition on the Carriage of Dangerous Goods Within a Cabin Occupied by Passengers

Dangerous goods must not be carried in the cabin of an aircraft occupied by passengers or on the flight deck, except as provided for in the Technical Instructions.

9.3.4	Prohibition on the Carriage of Passengers with ‘Cargo Aircraft Only’ Dangerous Goods

Dangerous goods identified as suitable for transport only on a cargo aircraft must not be carried on an aircraft on which passengers are being carried. In this context "passenger" excludes a crew member, an operator's employee (see 9.1.4 above), an authorised representative of an Authority and a person with duties in respect of a particular shipment of dangerous goods or other cargo on board.

9.3.5	Segregation and Separation

Dangerous goods must be loaded, stowed and secured on an aircraft as required by the Technical Instructions. This includes segregating packages from each other when they contain incompatible dangerous goods, the separation of explosives of different division numbers and compatibility groups (when required), securing packages in a manner that will prevent any movement, and on a cargo aircraft loading certain packages so they are accessible in flight. Packages of dangerous goods must also be protected so they cannot be damaged by the movement of baggage, mail, stores or other cargo.

Editorial Note: Operators holding approval for the carriage of dangerous goods should determine how such goods shall be secured to prevent movement in flight, to protect from damage by the movement of other items and to achieve adequate segregation whilst maintaining accesibility (if required) taking into account the types of aircraft operated and whether dangerous goods are to be carried underslung.  Additionally, it is appropriate to amend the following tables to reflect the operator’s policy towards the separation of dangerous goods from other cargo (e.g. toxic substances and foodstufffs).

### Segregation of incompatible dangerous goods

|  | Class or Division |
| --- | --- |
| Hazard Label | 1 | 2 | 3 | 4.2 | 4.3 | 5.1 | 5.2 | 6 | 8 | Animals, Foodstuffs or Feeds |
| 1 | Note 1 | Note 2 | Note 2 | Note 2 | Note 2 | Note 2 | Note 2 |  | Note 2 |  |
| 2 | Note 2 |  |  |  |  | X |  |  |  |  |
| 3 | Note 2 |  |  |  |  | X |  |  |  |  |
| 4.2 | Note 2 |  |  |  |  |  |  |  |  |  |
| 4.3 | Note 2 |  |  |  |  |  |  |  | X |  |
| 5.1 | Note 2 |  | X | X |  |  |  |  |  |  |
| 5.2 | Note 2 |  |  |  |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |  |  |  | Note 3 |
| 8 | Note 2 |  |  |  | X |  |  |  |  |  |
| Animals, Foodstuffs or Feeds |  |  |  |  |  |  |  | Note 3 |  |  |

An “X” at the intersection of a row and column indicates that packages containing these classes of dangerous goods may not be stowed next to or in contact with each other, or in a position which would allow interaction in the event of leakage of the contents. Thus, a package containing Class 3 dangerous goods may not be stowed next to or in contact with a package containing Division 5.1 dangerous goods. Packages containing dangerous goods with multiple hazards in the class or divisions which require segregation in accordance with the above table need not be segregated from other packages bearing the same UN number.

Note 1: See the table below detailing the separation of explosive substances and articles.

Note 2: This class or division must not be stowed together with explosives other than those in Division 1.4, Compatibility Group S.

Note 3: Substances of Class 6 (toxic and category A infectious substances) and substances requiring a subsidiary risk “Toxic” label must not be carried in the same compartment of an aircraft with animals, substances marked as or known to be foodstuffs, feeds or other edible substances intended for consumption by humans or by animals, unless either the toxic or category A infectious substances and the foodstuffs or animals are loaded in separate unit load devices and when stowed aboard the aircraft the unit load devices are not adjacent to each other, or the toxic or category A infectious substances are loaded in one closed unit load device and the foodstuffs or animals are loaded in another closed unit load device.

Editorial Note: Class 1 dangerous goods other than Division 1.4S may only be carried on cargo aircraft.  Operators not operating cargo aircraft should (a) delete the table explaining the separation of explosive substances and articles (below) and (b) amend Note 1 to the segregation table (above) to read ‘Only Division 1.4S is permitted for carriage on passenger aircraft’.

### Separation of explosive substances and articles

| Division and Compatibility Group | 1.3C | 1.3G | 1.4B | 1.4C | 1.4D | 1.4E | 1.4G | 1.4S |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1.3C |  |  | X |  |  |  |  |  |
| 1.3G |  |  | X |  |  |  |  |  |
| 1.4B | X | X |  | X | X | X | X |  |
| 1.4C |  |  | X |  |  |  |  |  |
| 1.4D |  |  | X |  |  |  |  |  |
| 1.4E |  |  | X |  |  |  |  |  |
| 1.4G |  |  | X |  |  |  |  |  |
| 1.4S |  |  |  |  |  |  |  |  |

An “X” at the intersection of a row and column indicates that explosives of these divisions and compatibility groups must be loaded into separate unit load devices and, when stowed aboard the aircraft, the unit load devices must be separated by other cargo with a minimum separation distance of 2 m. When not loaded in a unit load device, these explosives must be loaded into different, non-adjacent loading positions and separated by other cargo with a minimum separation distance of 2 m.  Explosive substances and articles carried under an exemption may be subject to additional separation requirements.

### 9.3.6	Loading of Dry Ice (JAR-OPS 3.1210(a))

Dry ice (Carbon dioxide, solid; UN1845) may be carried onboard aircraft to keep food (galley or cargo) and medicine or biological materials (as cargo) in a frozen or chilled condition. Carbon dioxide gas produced by the sublimation of dry ice is an asphyxiant and will reduce the amount of available oxygen to breathe. Dry ice sublimation producing excess CO2 gas may be dangerous in confined spaces where there is an absence of ventilation or ventilation rates are low. The signs and symptoms of CO2 poisoning are similar to those that precede lack of oxygen, namely headache, dizziness, muscular weakness, drowsiness, and ringing in the ears. CO2 poisoning does have a greater effect on breathing than simple lack of oxygen, causing a significant increase in the rate and depth of breathing as an early symptom. 10% carbon dioxide in air can be endured for only a few minutes whereas 12% to 15% would cause unconsciousness.

Editorial Note: Dry ice when shipped by itself or when used as a refrigerant for other commodities may be carried provided the operator has made suitable arrangements dependent on the aircraft type, the aircraft ventilation rates, the method of packing and stowing, whether animals will be carried on the same flight and other factors. To prevent the incapacitation of ground and aircrew, aircraft operators must specify maximum safe quantities of dry ice per compartment of the various aircraft types operated in accordance with the above criterion and information published by the applicable aircraft manufacturer(s).

### 9.3.7	Loading of Magnetised Material (JAR-OPS 3.1210(a))

Packing Instruction 953 allows the carriage  of such material when the magnetic field strength at a distance of 4.6 m causes a compass deflection of not more than 2 degrees (equivalent to 0.418 A/m or 0.00525 Gauss measured at a distance of 4.6 m). Material with a magnetic field strength exceeding these limits may only be carried with the prior approval of the State of Origin and the State of the Operator.

Magnetized material must be loaded so headings of aircraft compasses compasses are maintained within the tolerances prescribed by the applicable aircraft airworthiness requirements and, where practical, in locations minimising possible effects on compasses.

Note:	Masses of ferromagnetic metals such as automobiles, automobile parts, metal fencing, piping and metal construction material, even if not meeting the definition of magnetised materials, may affect compasses. As may packages or items of material which individually do not meet the definition of magnetised material, but cumulatively may have a magnetic field strength of a magnetised material.

Editorial Note: Operators should consider whether consignments of large quantities of ferromagnetic metals should be stowed as if they were classified as magnetised material. Operators, particularly of small aircraft, must establish adequate procedures to ensure that consignments described above are identified and loaded in a manner that will not affect aircraft instruments.

### 9.3.8	Loading of Radioactive Material (JAR-OPS 3.1210)

Editorial Note 1: Should there exist a policy not to carry radioactive material (stated within 9.1.1) this section may be omitted.

Radioactive materials are articles or substances which spontaneously and continuously emit ionising radiation, which can be harmful to the health of humans and animals and can affect photographic or X-Ray film. Whilst packagings used for the transport of radioactive material must provide protection from radiation, there is likely to be residual activity from packages offered for air transport.

A Transport Index (TI) is a number which represents the level of radiation at a distance of 1 metre, assigned to a single package, overpack or freight container. The TI is used to provide control over radiation exposure, to determine categories of radioactive material for the purposes of labelling, declaration, etc., to determine whether transport under exclusive use is required and to determine spacing requirements during storage and transport. The TI for each overpack or freight container must be determined as either the sum of the TIs of all the packages contained, or by direct measurement of radiation level.

Editorial Note 2: Operators that have a policy to carry radioactive materials must provide instructions on the loading of such dangerous goods based on the requirements for separation from persons, live animals and undeveloped photographic film below:

Separation From Persons

Categories II — Yellow and III — Yellow packages, overpacks or freight containers must be separated from persons. The minimum separation distances in the following table that are to be applied are based upon the sum of TIs and these distances are from the surface of the packages, overpacks or freight containers to the nearest inside surface of the passenger cabin or flight deck partitions or floors, irrespective of the duration of the carriage of the radioactive material. If the packages, overpacks or freight containers are separated into groups, the minimum distance from the nearest inside surface of the passenger cabin or flight deck partitions or floors to each group is the distance applicable to the sum of the TIs within the individual groups, provided that each group is separated from each other group by at least three times the distance applicable to the one that has the larger sum of TIs. Alternative separation distances apply when radioactive material is being carried by a cargo aircraft and in those circumstances the minimum distances must be applied as above and also to any other areas occupied by persons. Whether carried on a passenger or cargo aircraft, in accordance with the practise of keeping exposure to radiation as low as reasonable achievable, separation distances should be extended whenever feasible.

Editorial Note: The highest minimum distances in the following tables are included to provide for the carriage of radioactive material within very large helicopters and underslung loads. The higher figures may be removed if inappropriate to the specific operation.

| Passenger or Cargo Aircraft |  | Cargo Aircraft Only |  |
| --- | --- | --- | --- |
| Total sum of transport indexes | Minimum distance (metres) | Total sum of transport indexes | Minimum distance (metres) |
| 0.1 - 1.0 | 0.30 | 50.1 - 60.0 | 4.65 |
| 1.1 - 2.0 | 0.50 | 60.1 - 70.0 | 5.05 |
| 2.1 - 3.0 | 0.70 | 70.1 - 80.0 | 5.45 |
| 3.1 - 4.0 | 0.85 | 80.1 - 90.0 | 5.80 |
| 4.1 - 5.0 | 1.00 | 90.1 - 100.0 | 6.10 |
| 5.1 - 6.0 | 1.15 | 100.1 - 110.0 | 6.45 |
| 6.1 - 7.0 | 1.30 | 110.1 - 120.0 | 6.70 |
| 7.1 - 8.0 | 1.45 | 120.1 - 130.0 | 7.00 |
| 8.1 - 9.0 | 1.55 | 130.1 - 140.0 | 7.30 |
| 9.1 - 10.0 | 1.65 | 140.1 - 150.0 | 7.55 |
| 10.1 - 11.0 | 1.75 | 150.1 - 160.0 | 7.80 |
| 11.1 - 12.0 | 1.85 | 160.1 - 170.0 | 8.05 |
| 12.1 - 13.0 | 1.95 | 170.1 - 180.0 | 8.30 |
| 13.1 - 14.0 | 2.05 | 180.1 - 190.0 | 8.55 |
| 14.1 - 15.0 | 2.15 | 190.1 - 200.0 | 8.75 |
| 15.1 - 16.0 | 2.25 | 200.1 - 210.0 | 9.00 |
| 16.1 - 17.0 | 2.35 | 210.1 - 220.0 | 9.20 |
| 17.1 - 18.0 | 2.45 | 220.1 - 230.0 | 9.40 |
| 18.1 - 20.0 | 2.60 | 230.1 - 240.0 | 9.65 |
| 20.1 - 25.0 | 2.90 | 240.1 - 250.0 | 9.85 |
| 25.1 - 30.0 | 3.20 | 250.1 - 260.0 | 10.05 |
| 30.1 - 35.0 | 3.50 | 260.1 - 270.0 | 10.25 |
| 35.1 - 40.0 | 3.75 | 270.1 - 280.0 | 10.40 |
| 40.1 - 45.0 | 4.00 | 280.1 - 290.0 | 10.60 |
| 45.1 - 50.0 | 4.25 | 290.1 - 300.0 | 10.80 |

Separation From Live Animals

Categories II — Yellow and III — Yellow packages, overpacks or freight containers must be separated from live animals by a distance of at least 0.5 metres for journeys not exceeding 24 hours, and by a distance of at least 1.0 metres for journeys longer than 24 hours.

Separation From Undeveloped Photographic Film

Categories II — Yellow and III — Yellow packages, overpacks or freight containers must be separated from undeveloped photographic films or plates. The minimum separation distances (metres) to be applied from the surface of the packages, overpacks or freight containers to the surface of the packages of undeveloped photographic films or plates are as follows:

|  | Duration of carriage |
| --- | --- |
| Total sum of transport indexes | 2 hours or less | 2-4 hours | 4-8 hours | 8-12 hours | 12-24 hours | 24-48 hours |
| 1 | 0.4 | 0.6 | 0.9 | 1.1 | 1.5 | 2.2 |
| 2 | 0.6 | 0.8 | 1.2 | 1.5 | 2.2 | 3.1 |
| 3 | 0.7 | 1.0 | 1.5 | 1.8 | 2.6 | 3.8 |
| 4 | 0.8 | 1.2 | 1.7 | 2.2 | 3.1 | 4.4 |
| 5 | 0.8 | 1.3 | 1.9 | 2.4 | 3.4 | 4.8 |
| 10 | 1.4 | 2.0 | 2.8 | 3.5 | 4.9 | 6.9 |
| 20 | 2.0 | 2.8 | 4.0 | 4.9 | 6.9 | 10.0 |
| 30 | 2.4 | 3.5 | 4.9 | 6.0 | 8.6 | 12.0 |
| 40 | 2.9 | 4.0 | 5.7 | 6.9 | 10.0 | 14.0 |
| 50 | 3.2 | 4.5 | 6.3 | 7.9 | 11.0 | 16.0 |

Note:	The above table is calculated so that the radiation dose received by the films does not exceed 0.1 mSv (10 mrem).

Means of Securing

The means of securing packages or overpacks must adequately ensure that minimum separation distances are maintained at all times.

Editorial Note: An aircraft and equipment used regularly for the transport of radioactive material must be periodically checked to determine the level of contamination. The frequency of such checks must be related to the likelihood of contamination and the extent to which radioactive material is transported. Operators that carry radioactive material need to define the means and frequency of checks for radioactive contamination of aircraft and equipment (e.g. unit load devices).

### 9.3.9	Notification to Captain (NOTOC) (JAR-OPS 3.1215(d))

The operator of an aircraft in which dangerous goods are to be carried must provide the pilot-in-command, as early as practicable before departure of the aircraft, with accurate and legible written or printed information concerning dangerous goods that are to be carried as cargo.

Note:	This includes information about dangerous goods loaded at a previous departure point and which are to be carried on the subsequent flight.

This information must include the following:

a)	the air waybill number (when issued);

b)	the proper shipping name (supplemented with the technical name(s) if appropriate;

c)	the class or division, and subsidiary risk(s) corresponding to the subsidiary risk label(s) applied, by numerals, and (in the case of Class 1) the compatibility group;

d)	the packing group shown on the dangerous goods transport document;

e)	the number of packages and their exact loading location. For radioactive material see (g) below;

f)	the net quantity, or gross mass if applicable, of each package, except that this does not apply to radioactive material or other dangerous goods where the net quantity or gross mass is not required on the dangerous goods transport document. For a consignment consisting of multiple packages containing dangerous goods bearing the same proper shipping name and UN number, only the total quantity and an indication of the quantity of the largest and smallest package at each loading location need to be provided;

g)	for radioactive material the number of packages, overpacks or freight containers, their category, their Transport Index (if applicable) and their exact loading location;

h)	whether the package must be carried on cargo aircraft only;

i)	the aerodrome at which the package(s) is to be unloaded; and

j)	where applicable, an indication that the dangerous goods are being carried under a State exemption.

Note:	For UN 1845 Carbon dioxide, solid (dry ice), only the UN number, proper shipping name, class, total quantity in each hold on the aircraft and the aerodrome at which the package(s) is to be unloaded need to be provided.

Editorial Note: the telephone number where a copy of the information to the pilot-in-command can be obtained during the flight is additionally required on the NOTOC should it be intended to make it possible for the pilot-in-command to provide the appropriate Air Traffic Services Unit with a telephone number instead of details about the dangerous goods on board the aircraft in the event of an in-flight emergency.

9.3.10	Availability of NOTOC on the Ground for the Duration of Flight

A legible copy of the information to the pilot-in command must be retained on the ground. This copy must have an indication on it, or with it, that the pilot-in-command has received the information. This copy, or the information contained in it, must be readily accessible to the aerodromes of last departure and next scheduled arrival point, until after the flight to which the information refers. This is to facilitate notifying emergency services and authorities of the dangerous goods on board in the event of an aircraft accident or incident (see 11.10.2).

Editorial Note: Operators should establish how accessibility of NOTOCs on the ground at airports of departure and destination for the duration of flight is to be achieved, taking into account relevant factors, such as the closure of a freight shed holding the documentation before the completion of a flight. Particular attention should be paid to the arrangements for ad hoc charters carrying dangerous goods where ongoing instructions to ensure the availability of the NOTOC may not be in place, e.g. through issuing appropriate instructions within the ground handling request.

9.3.11	Retention of Documents

At least one copy of the documents appropriate to the transport by air of a consignment of dangerous goods must be retained for a minimum period of three months, or such other period as specified by the States concerned, after the flight on which the dangerous goods were transported. As a minimum, the documents which must be retained are the dangerous goods transport document (Shipper’s Declaration), the acceptance checklist and the NOTOC.

Editorial Note: Operators should indicate where the documents appropriate to the transport by air of a consignment of dangerous goods are to be retained, e.g. within a flight file, or within the files of a handling agent(s), etc. If this to be carried out by a handling agent, procedures need to be in place, particularly for ad hoc charters.

### 9.3.12	Ad Hoc Charters (JAR-OPS 3.1215)

Editorial Note: Many operators utilise ground handling agents to discharge certain duties with regards to the carriage of dangerous goods by air, e.g. conducting acceptance checks, NOTOC preparation and administration, aircraft loading, retention of documents, etc. Should such operators wish to undertake ad hoc charters involving the carriage of dangerous goods between stations where ongoing ground handling agreements are not in place, it would be necessary for duties to be properly assigned to the agent(s) concerned in advance of the operation of flights. Furthermore, should the agent at the station of departure not operate 24 hours a day, it must also be ensured that a copy of the NOTOC is readily available on the ground in the event of an emergency, e.g. by instructing the agent to fax or e-mail a copy of the completed NOTOC to the operator as soon as possible after the signature by the pilot-in-command has been obtained. Procedures for assigning such duties to agents (such as via the issue of ad hoc ground handling requests) should be established.

### Recognition of Undeclared / Hidden Dangerous Goods (JAR-OPS 3.1225(b))

      - 9.4.1	‘Hidden’ Dangerous Goods

Personnel must be alert to indications that undeclared dangerous goods are present within cargo, mail or stores. Personnel interfacing with passengers must be alert to indications that prohibited dangerous goods are carried by passengers or within their baggage.

NOTE:	THE DISCOVERY OF UNDECLARED OR MIS-DECLARED DANGEROUS GOODS OR THE DISCOVERY OF DANGEROUS GOODS FORBIDDEN FOR CARRIAGE BY PASSENGERS (DISCOVERED AFTER THE CHECK-IN PROCESS) MUST BE REPORTED TO THE CAA – SEE 11.10.4.

The following is a list of general descriptions that are often used for items in cargo or in passengers’ baggage and the types of dangerous goods that may be included in any item bearing that description.

Aircraft on ground (AOG) spares — may contain explosives (flares or other pyrotechnics), chemical oxygen generators, unserviceable tyre assemblies, cylinders of compressed gas (oxygen, carbon dioxide or fire extinguishers), fuel in equipment, wet or lithium batteries, matches.

Automobile parts (car, motor, motorcycle) — may include engines, carburettors or fuel tanks that contain or have contained fuel, wet batteries, compressed gases in tyre inflation devices and fire extinguishers, air bags, etc.

Breathing apparatus — may indicate cylinders of compressed air or oxygen, chemical oxygen generators or refrigerated liquefied oxygen.

Camping equipment — may contain flammable gases (butane, propane, etc.), flammable liquids (kerosene, gasoline, etc.) or flammable solids (hexamine, matches, etc.).

Cars, car parts — see automobile parts, etc.

Chemicals — may contain items meeting any of the criteria for dangerous goods, particularly flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Consolidated consignments (groupages) — may contain any of the defined classes of dangerous goods.

Cryogenic (liquid) — indicates refrigerated liquefied gases such as argon, helium, neon, nitrogen, etc.

Cylinders — may contain compressed or liquefied gas.

Dental apparatus — may contain flammable resins or solvents, compressed or liquefied gas, mercury and radioactive material.

Diagnostic specimens — may contain infectious substances.

Diving equipment — may contain cylinders of compressed gas (e.g. air or oxygen). May also contain high intensity diving lamps that can generate extreme heat when operated in air. In order to be carried safely, the bulb or battery should be disconnected.

Drilling and mining equipment — may contain explosive(s) and/or other dangerous goods.

Dry shipper (vapour shipper) — may contain free liquid nitrogen. Dry shippers are only not subject to these Instructions when they do not permit the release of any free liquid nitrogen irrespective of the orientation of the packaging.

Electrical equipment — may contain magnetised materials, mercury in switch gear, electron tubes or wet batteries.

Electrically-powered apparatus (wheelchairs, lawn mowers, golf carts, etc.) — may contain wet batteries.

Expeditionary equipment — may contain explosives (flares), flammable liquids (gasoline), flammable gas (camping gas) or other dangerous goods.

Film crew and media equipment — may contain explosive pyrotechnic devices, generators incorporating internal combustion engines, wet batteries, fuel, heat-producing items, etc.

Frozen embryos — may be packed in refrigerated liquefied gas or dry ice.

Frozen fruit, vegetables, etc. — may be packed in dry ice (solid carbon dioxide).

Fuel control units — may contain flammable liquids.

Hot-air balloon — may contain cylinders with flammable gas, fire extinguishers, engines (internal combustion), batteries, etc.

Household goods — may contain items meeting any of the criteria for dangerous goods. Examples include flammable liquids such as solvent-based paint, adhesives, polishes, aerosols (for passengers, those not permitted under ICAO Technical Instructions 8;1.1.2), bleach, corrosive oven or drain cleaners, ammunition, matches, etc.

Instruments — may conceal barometers, manometers, mercury switches, rectifier tubes, thermometers, etc. containing mercury.

Laboratory/testing equipment — may contain items meeting any of the criteria for dangerous goods, particularly flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Machinery parts — may contain flammable adhesives, paints, sealants and solvents, wet and lithium batteries, mercury, cylinders of compressed or liquefied gas, etc.

Magnets and other items of similar material — may individually or cumulatively meet the definition of magnetised material.

Medical supplies — may contain items meeting any of the criteria for dangerous goods, particularly flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Metal construction material — may contain ferro-magnetic material which may be subject to special stowage requirements due to the possibility of affecting aircraft instruments.

Metal fencing — may contain ferro-magnetic material which may be subject to special stowage requirements due to the possibility of affecting aircraft instruments.

Metal piping — may contain ferro-magnetic material which may be subject to special stowage requirements due to the possibility of affecting aircraft instruments.

Passengers’ baggage — may contain items meeting any of the criteria for dangerous goods. Examples include fireworks, flammable household liquids, corrosive oven or drain cleaners, flammable gas or liquid lighter refills or camping stove cylinders, matches, ammunition, bleach, aerosols not permitted (toxic, etc.).

Pharmaceuticals — may contain items meeting any of the criteria for dangerous goods, particularly radioactive material, flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Photographic supplies — may contain items meeting any of the criteria for dangerous goods, particularly heat-producing devices, flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Racing car or motorcycle team equipment — may contain engines, carburettors or fuel tanks that contain fuel or residual fuel, wet batteries, flammable aerosols, nitromethane or other gasoline additives, cylinders of compressed gases, etc.

Refrigerators — may contain liquefied gases or an ammonia solution.

Repair kits — may contain organic peroxides and flammable adhesives, solvent-based paints, resins, etc.

Samples for testing — may contain items meeting any of the criteria for dangerous goods, particularly infectious substances, flammable liquids, flammable solids, oxidisers, organic peroxides, toxic or corrosive substances.

Semen — may be packed with dry ice or refrigerated liquefied gas (see also dry shipper).

Swimming pool chemicals — may contain oxidising or corrosive substances.

Switches in electrical equipment or instruments — may contain mercury.

Tool boxes — may contain explosives (power rivets), compressed gases or aerosols, flammable gases (butane cylinders or torches), flammable adhesives or paints,  corrosive liquids, etc.

Torches — micro torches and utility lighters may contain flammable gas and be equipped with an electronic starter. Larger torches may consist of a torch head (often with a self-igniting switch) attached to a container or cylinder of flammable gas.

Unaccompanied passengers’ baggage/personal effects — may contain items meeting any of the criteria for dangerous goods. Examples include fireworks, flammable household liquids, corrosive oven or drain cleaners, flammable gas or liquid lighter refills or camping stove cylinders, matches, bleach, aerosols, etc.

Note: Excess baggage carried as cargo may contain certain dangerous goods (see 9.1.3.4).

Vaccines — may be packed in dry ice (solid carbon dioxide).

      - Identification of Dangerous Goods Through X-Ray Screening

Persons conducting security screening of cargo should be alert to the presence of dangerous goods within packages that are not marked and labelled as dangerous goods and/or not accompanied by a Shipper’s Declaration. In particular, items such as aerosols, ammunition, gas cylinders (camping gas, cylinders attached to life-jackets, etc.), cigarette lighters and wet acid batteries can be readily identified from x-ray images. Information provided on an air waybill or marked on a package often indicates that a consignment contains no dangerous goods. In the absence of such annotation by the shipper, should suspicions be raised by the size and shape of the contents of a package, consideration should be given to opening and hand-searching the consignment to verify that no undeclared dangerous goods are present.

Consignments of dangerous goods that have been properly marked, labelled and declared to the operator (where approved for carriage) are commonly processed separately from general freight. Should consignments bearing UN numbers, proper shipping names or hazard labels be discovered within general freight, when separate arrangements exist, this should be queried. It may be that no shipper’s declaration accompanies the consignment; as such the consignment of dangerous goods would be considered ‘undeclared’.

      - Safety Data Sheets

REACH (Registration, Evaluation, Authorisation & restriction of CHemicals) is a European Union regulation controlling chemicals in Europe. REACH requires for many substances and mixtures, a Safety Data Sheet (SDS) to be provided either before or at the time of first delivery.  Section 14 of the EU format SDS provides basic classification information, i.e. UN number, proper shipping name, Class/Division and Packing Group.

      - GHS/CHIP Consumer Labelling

Some everyday household items bear consumer warning labels which may or may not indicate they are classified as dangerous goods in air transport. All over the world there are different laws on how to identify the hazardous properties of chemicals (called ‘classification’) and how information about these hazards is then passed to users (through consumer supply labels and safety data sheets for workers).  This can be confusing because the same chemical can have different hazard descriptions in different countries. For example, a chemical could be labelled for supply as ‘toxic’ in one country, but not in another.  For this reason, the UN brought together experts from different countries to create the Globally Harmonized System of Classification and Labelling of Chemicals (GHS).

Within Europe the Regulation on Classification, Labelling and Packaging of Substances and Mixtures (known as the CLP Regulation) provides a transitional period to allow a gradual migration to the GHS regime.  The Regulation already applies to the classification of substances and will apply to mixtures from 1 June 2015.   In the meantime suppliers in the UK may continue to label goods according to the Chemicals (Hazard Information and Packaging for Supply) Regulations (CHIP).  However, they may as an alternative choose to classify, label and package mixtures according to CLP.  There are, therefore, two systems of consumer supply labelling that may indicate the presence of dangerous goods.

      - GHS Labels

Products bearing the following GHS labels ARE classified as dangerous goods:

Note: A product bearing the GHS corrosive label (depicted far right above) is NOT classified as dangerous goods if the signal word ‘Danger’ and hazard statement ‘causes serious eye damage’ applies.

Products bearing the following GHS labels are NOT classified as dangerous goods:

      - CHIP Labels

CHIP labels are represented below together with indications of how goods bearing such labels may be classified for transport purposes.  In the event that CHIP labels and associated risk phrases cause suspicion that a particular consignment contains undeclared dangerous goods, it will be necessary to refer to the Safety Data Sheet applicable to the product (see information above).

##### Physiochemical

| Symbol | Abbreviation | Hazard | Description of hazard | Transport classification |
| --- | --- | --- | --- | --- |
|  | E | explosive | Chemicals that explode. | All substances and preparations classified in Class 1. Organic peroxides of Division 5.2 which require an "EXPLOSIVE" subsidiary risk label. |
|  | O | oxidising | Chemicals that react exothermically with other chemicals. | All substances and preparations classified in Division 5.1. All organic peroxides of Division 5.2 other than those which require an "EXPLOSIVE" subsidiary risk label. |
|  | F+ | extremely flammable | Chemicals that have an extremely low flash point and boiling point, and gases that catch fire in contact with air. | Gases of Division 2.1 and Division 2.3 gases with a subsidiary risk of Division 2.1. All substances and preparations classified in Class 3 Packing Group I. |
|  | F | highly flammable | Chemicals that may catch fire in contact with air, only need brief contact with an ignition source, have a very low flash point or evolve highly flammable gases in contact with water. | Most substances and preparations classified as Class 3 Packing Group II. Some solids classified in Division 4.1. All substances and preparations classified in Division 4.2. All substances and preparations classified as Division 4.3. |
| None | None | flammable | Substances and preparations with a flashpoint equal to or greater than 21°C and less than or equal to 55°C. | Some substances and preparations classified as Class 3 Packing Group II and most substances and preparations classified in Class 3 Packing Group III. |

##### Health

| Symbol | Abbreviation | Hazard | Description of hazard | Transport classification |
| --- | --- | --- | --- | --- |
|  | T+ | very toxic | Chemicals that at very low levels cause damage to health. | Substances and preparations classified in Division 6.1 Packing Group I, and some substances and preparations classified in Division 6.1 Packing Group II. |
|  | T | toxic | Chemicals that at low levels cause damage to health. | Substances and preparations classified in Division 6.1 Packing Group II other than those classified above, and some substances and preparations classified in Division 6.1 Packing Group III. |
|  | Carc Cat 1 | category 1 carcinogens | Chemicals that may cause cancer or increase its incidence. | Substances and preparations may be classified in any Class or Division of Classes 1 to 9 (though normally in Division 6.1) but may, however, be not subject to the Technical Instructions and may not need to be declared as dangerous goods. |
|  | Carc Cat 2 | category 2 carcinogens |  |  |
|  | Carc Cat 3 | category 3 carcinogens |  |  |
|  | Muta Cat 1 | category 1 mutagens | Chemicals that induce heritable genetic defects or increase their incidence. |  |
|  | Muta Cat 2 | category 2 mutagens |  |  |
|  | Muta Cat 3 | category 3 mutagens |  |  |
|  | Repr Cat 1 | category 1 reproductive toxins | Chemicals that produce or increase the incidence of birth defects, which may be severe, and/or an impairment in reproductive functions or capacity |  |
|  | Repr Cat 2 | category 2 reproductive toxins |  |  |
|  | Repr Cat 3 | category 3 reproductive toxins |  |  |
|  | Xn | harmful | Chemicals that may cause damage to health. | Substances and preparations classified in Division 6.1 Packing Group III other than those classified above, and some substances and preparations which are not subject to the Technical Instructions. |
|  | C | corrosive | Chemicals that may destroy living tissue on contact. | The vast majority of substances and preparations which are classified as Class 8. |
|  | Xi | irritant | Chemicals that may cause inflammation to the skin or other mucous membranes. | Some organic peroxides of Division 5.2. Otherwise, substances and preparations are not subject to the Technical Instructions. |

##### Environmental

| Symbol | Abbreviation | Hazard | Description of hazard | Transport classification |
| --- | --- | --- | --- | --- |
|  | N | dangerous for the environment | Chemicals that may present an immediate or delayed danger to one or more components of the environment. | Substances designated as severe marine pollutants(a), marine pollutants(b), and aquatic pollutants(c). Substances and preparations may be classified in any Class or Division of Classes 1 to 8, and UN 3077 and UN 3082 in Class 9. |

Notes:

(a)	Substances and preparations designated as "severe marine pollutant" in the International Maritime Dangerous Goods Code.

(b)	Substances and preparations designated as "marine pollutant" in the International Maritime Dangerous Goods Code.

(c)	Substances and preparations designated as aquatic pollutants in ADR.

(d)	The above table does not apply to substances and preparations of Division 6.2 and Class 7 which are not subject to the CHIP Regulations.

(e)	CHIP labels for mixtures will be replaced by the Globally Harmonized System (GHS) of labelling on 1 June 2015.  Information on CHIP should be removed after 1 June 2017 once transitional arrangements cease to apply.

9.5	Emergency Situations

### 9.5.1	Provision of Information for Use in Responding to In-Flight Emergencies (JAR-OPS 3.1215(c))

For those dangerous goods for which a dangerous goods transport document is required, the commander of an aircraft carrying such goods must be provided with information which can be used on board to assist in planning the response to an emergency arising in-flight involving the dangerous goods.

Editorial Note: This information can be provided by the ‘Emergency Response Guidance for Aircraft Incidents Involving Dangerous Goods’ (Doc 9481), which is published by the International Civil Aviation Organization, or by another document giving similar information. Operators should establish what information is to be made available to flight crew onboard aircraft.

## 9.5.2	Procedures for Responding to Emergency Situations (JAR-OPS 3.1215(e))

For procedures for responding to emergency situations see section 11.10.

## 9.6	Conditions Under Which Weapons, Munitions of War and Sporting Weapons May Be Carried (JAR-OPS 3.070 and ANO)

9.6.1	Need for Approval to Transport Munitions of War

Weapons of war and munitions of war can only be carried provided an approval to do so has been granted by all the States concerned before a flight. They must be carried in the aircraft in a place which is inaccessible to passengers during flight and, in the case of firearms, unloaded, except as specified in 9.5.2 below.

Editorial Note 1: Insert Text [Operator Name holds/does not hold] CAA approval for the transport of Munitions of War by air.

9.6.2	Stowage Requirements for Munitions of War

In exceptional circumstances weapons of war and munitions of war may be carried other than in an inaccessible place on the aircraft and may be loaded, provided an approval to do so has been granted by all the States concerned before a flight. These exceptional circumstances are intended primarily to permit the carriage of law enforcement officers, protection officers, etc.

UK Police Protection Officers hold an exemption from the Air Navigation Order that enables them to carry their weapons on their person when accompanying specific named VIPs. A condition on the exemption requires the police to provide the operator with a copy of the relevant exemption in advance of the flight to demonstrate that the exemption applies to them and the person they are accompanying. Official Record Series 4 approves the carriage of weapons by operators in accordance with the exemption issued to UK Police Protection Officers. Should an operator be asked to carry protection officers bearing weapons on their person and the Police do not/cannot provide a copy of the relevant exemptions (preferably when booking the flight), then their weapons must be stowed in a location that is inaccessible during flight. When the police officer is not accompanying any of the persons referred to in the exemption, the unloaded arms and ammunition shall be stowed in a location which is inaccessible to passengers on the aircraft. The exemption issued to UK Police Protection Officers and the Official Record Series 4 document each contain additional conditions with which operators must comply.

There are some limited occasions when the UK CAA may grant one-off exemptions for persons not on the two exemptions held by the Police, such as visiting Heads of State, but these will generally only be when accompanied by UK Protection Officers. In such circumstances, or in the event of a request for non-UK protection officers to carry weapons in the cabin, the operator must apply to the CAA Dangerous Goods Office.

9.6.3	Notifying Commander of the Carriage of Munitions of War

The commander must be notified before a flight if weapons of war or munitions of war are to be carried on the aircraft.

9.6.4	Carriage of Sporting Weapons When Inaccessible to Passengers During Flight

Sporting weapons and ammunition for such weapons may be carried without an approval from an Authority, provided they are stowed in a place on the aircraft which is inaccessible to passengers during flight and, in the case of firearms, unloaded.

NOTE: Ammunition is subject to the conditions set out in 9.1.5.

Editorial Note: Operators must take all reasonable measures to ensure that any sporting weapons intended to be carried by air are reported to them and operators should describe the measures in place to make passengers aware of the need to furnish the operator with details of any sporting weapon they intend to carry.

9.6.5	Carriage of Sporting Weapons Other Than In An Inaccessible Location

With the agreement of the CAA sporting weapons and ammunition may be carried other than in an inaccessible location on an aircraft if it has been accepted that it is impracticable so to do, subject to any conditions stipulated by the CAA.

Editorial Note: Operators should describe any agreements in place for the carriage of weapons other than in an inaccessible location on an aircraft. Where aircraft types are operated that do not have stowage locations that are inaccessible during flight, in the absence of other procedures for the stowage of weapons having been accepted by the CAA, sporting weapons may not be carried on these aircraft and this should be stipulated accordingly (see also IEM 3.070).

9.6.6	The passenger and operator (or his agent) must observe all regulations applicable to the export, import and transit of weapons and ammunition, applicable in the country of departure, transit and destination.

Editorial Note 1: Operators should consider all relevant legislation when formulating procedures for the carriage of weapons, munitions of war and sporting weapons.

Editorial Note 2: Guidance regarding the transport of dangerous goods and munitions of war is available within CAP 668 Transport by Air of Dangerous Goods, Munitions of War, Sporting Weapons and Animals - Guidance Material on the Operator's Responsibilities.

## 11.10 	Special Notification Requirements in the Event of an Accident or Occurrence When Dangerous Goods are Being Carried or Have Been Offered for Air Transport Without Having Been Prepared and Declared in Accordance with the ICAO Technical Instructions (JAR-OPS 3.1215(e) and 3.1225)

### 11.10.1	Information to be Provided by the Pilot-In-Command in the Event of an In-Flight Emergency (ICAO Technical Instructions 7;4.3)

If an in-flight emergency occurs and the situation permits the commander must inform the appropriate Air Traffic Services Unit of any dangerous goods on board. This information should include the proper shipping name, class/division, identified subsidiary risk(s), compatibility group for explosives, quantity and location on board.

Editorial Note: If it is the operator’s policy to provide flight crew with a telephone number where detailed information on dangerous goods on board may be obtained (on the NOTOC) this procedure should be explained.

### 11.10.2	Information to be Provided by the Operator in the Event of an Aircraft Accident or Serious Incident Where Dangerous Goods Carried as Cargo May be Involved (JAR-OPS 3.1215(e)(2))

If an aircraft carrying dangerous goods as cargo is involved in an accident or serious incident where the dangerous goods may be involved, the operator must provide information, without delay, to emergency services responding to the accident or serious incident about the dangerous goods on board, as shown on the copy of the information to the pilot-in-command (NOTOC). The information must be sufficient to enable any hazards created by the dangerous goods to be minimised and include the proper shipping name, UN number, class/division, any identified subsidiary risks, the compatibility group for explosives, the quantity and the location on board the aircraft. As soon as possible, the operator must also provide this information to the CAA Dangerous Goods Office and the appropriate authority of the State in which the accident or serious incident occurred. In the first instance, the Dangerous Goods Office should be alerted to the incident or accident by phone using the following number:

Telephone: +44 (0) 1293 573800.

### 11.10.3	Information to be Provided by the Operator in the Event of an Aircraft Incident (JAR-OPS 3.1215(e)(1))

In the event of an aircraft incident, the operator of an aircraft carrying dangerous goods as cargo must, if requested to do so, provide information without delay to the emergency services responding to the incident and to the appropriate authority of the State in which the incident occurred, about the dangerous goods on board, as shown on the copy of the information to the pilot-in-command (NOTOC). For aircraft accidents and serious incidents, see 11.10.2.

### 11.10.4	Dangerous Goods Accident and Incident Reports (JAR-OPS 3.1225)

Definition of dangerous goods accident: An occurrence associated with and related to the transport of dangerous goods by air which results in fatal or serious injury to a person or major property or environmental damage.

Definition of dangerous goods incident: An occurrence other than a dangerous goods accident associated with and related to the transport of dangerous goods by air, not necessarily occurring on board an aircraft, which results in injury to a person, property or environmental damage, fire, breakage, spillage, leakage of fluid or radiation or other evidence that the integrity of the packaging has not been maintained. Any occurrence relating to the transport of dangerous goods which seriously jeopardises an aircraft or its occupants is also deemed to be a dangerous goods incident.

Note:	A dangerous goods accident or incident may also constitute an aircraft accident or incident as specified in ICAO Annex 13 — Aircraft Accident and Incident Investigation.

In addition to the requirements stated in the ICAO Technical Instructions for the reporting of dangerous goods occurrences, OPS 1.420 and the Air Navigation Order require that any incident which endangers or which, if not corrected, would endanger an aircraft, its occupants or any other person is reported to CAA Safety Data the CAA in accordance with CAP 382.  Dangerous goods occurrences reportable under the Mandatory Occurrence Reporting Scheme include:

- Dangerous goods found not to have been secured to prevent movement

- Damage to packages of dangerous goods

- NOTOC errors where dangerous goods have not been stowed in accordance with loading instructions

- Failure to prepare electric wheelchairs in order to prevent accidental activation

- Electric wheelchairs found not to have been stowed and secured correctly

- Leakage of dangerous goods from passenger baggage

NOTE: Dangerous goods occurrences meeting the MOR criteria also meet the definition of a dangerous goods accident or incident (above), reportable in accordance with OPS 1.1225.  Accordingly, the report must be made to CAA Safety Data within 72 hours (rather than 96), unless exceptional circumstances prevent this.

A dangerous goods accident or dangerous goods incident not meeting the MOR criteria must be reported to the CAA Dangerous Goods Office within 72 hours, unless exceptional circumstances prevent this. If necessary, a subsequent report shall be made as soon as possible giving all the details that were not known at the time the first report was sent. If a report has been made verbally, written confirmation shall be sent as soon as possible. Any type of accident or incident must be reported irrespective of whether the dangerous goods are in cargo, mail, stores, passengers’ baggage or crew baggage.

An operator must report any occasion when undeclared or misdeclared dangerous goods are discovered in cargo, mail or stores. Such a report must be made to the appropriate authorities of the State of the Operator and the State in which this occurred. An operator must also report any occasion when dangerous goods that are not permitted are discovered in passengers’ baggage or on their person after the passenger has checked in for the flight concerned. Such a report must be made to the appropriate authority of the State in which this occurred.

Report forms are available via the Publications section at www.caa.co.uk

Dangerous goods occurrences meeting the MOR Criteria are to be reported using CAA Form SRG 1601 (or similar).

Dangerous goods occurrences (not meeting the MOR criteria) may be reported using the following forms:

CAA Form SRG 2808 may be used to report a dangerous goods occurrence involving cargo or unaccompanied baggage.

CAA Form SRG 2809 may be used to report a dangerous goods occurrence involving a passenger/crew member or their baggage.

The first and any subsequent report shall be as precise as possible and contain such of the following data that are relevant:

- Date of the incident or accident or the finding of undeclared or misdeclared dangerous goods.

- Location, the flight number and flight date.

- Description of the goods and the reference number of the air waybill, pouch, baggage tag, ticket, etc.

- Proper shipping name (including the technical name, if appropriate) and UN/ID number, when known.

- Class or division and any subsidiary risk.

- Type of packaging, and the packaging specification marking on it.

- Quantity of dangerous goods.

- Name and address of the shipper, passenger, etc.

- Any other relevant details.

- Suspected cause of the incident or accident.

- Action taken.

- Any other reporting action taken.

- Name, title, address and telephone number of the person making the report.

Copies of relevant documents and any photographs taken should be attached to a report.

NOTE:	IF SAFE TO DO SO, THE DANGEROUS GOODS INVOLVED IN THE ACCIDENT OR INCIDENT SHOULD BE HELD PENDING CAA INVESTIGATION.

Editorial Note: Operators should describe their procedures for reporting dangerous goods incidents, accidents and undeclared dangerous goods to the CAA. Where applicable, this information should be provided to handling agents so that, as a minimum, they are advised to whom non-MOR events should be submitted (the Air Navigation Order places a direct legal duty upon a person who performs a function in respect of the ground handling of aircraft to report to the CAA any incident which endangers or which, if not corrected, would endanger an aircraft, its occupants or any other person).

### 11.10.5	Removal of Contamination (JAR-OPS 3.1205)

In the event of a spillage or leakage of dangerous goods within an aircraft, the position where the dangerous goods or unit load device was stowed on the aircraft must be inspected for damage or contamination and any hazardous contamination removed. The hazard of the dangerous goods within packages concerned may be established by checking the entry on the NOTOC for that loading position or from hazard labels applied to the packages. Persons responding in the event of damage to or leakage of dangerous goods from packages must:

- identify the hazards and wear appropriate protective clothing;

- avoid handling the package or keep handling to a minimum;

- inspect adjacent packages for contamination and put aside any that may have been contaminated;

- arrange for decontamination of the aircraft and equipment; and

- in the case of infectious material, inform the appropriate public health authority or veterinary authority, and provide information to any other countries of transit where persons may have been exposed to danger; and notify the shipper and/or the consignee.

If it is evident that a package containing radioactive material is damaged or leaking, or if it is suspected that the package may have leaked or been damaged, access to the package must be restricted and a qualified person must, as soon as possible, assess the extent of contamination and the resultant radiation level of the package. The scope of the assessment must include the package, the aircraft, the adjacent loading and unloading areas and, if necessary, all other material which has been carried in the aircraft. When necessary, additional steps for the protection of persons, property and the environment must be taken in accordance with provisions established by the relevant competent authority, to overcome and minimise the consequences of such leakage or damage. A helicopter which has been contaminated by radioactive materials must be immediately taken out of service and not returned until the radiation level at any accessible surface and the non-fixed contamination are not more than the values specified in the Technical Instructions. In the event of non-compliance with any limit in the Technical Instructions applicable to radiation level or contamination, the operator must ensure the shipper is informed if the non-compliance is identified during transport; take immediate steps to mitigate the consequences of the non-compliance; and communicate the non-compliance to the shipper and relevant competent Authority(ies), respectively, as soon as practicable and immediately whenever an emergency situation has developed or is developing.

# SECTION D 2.4

# TRAINING SYLLABUS FOR TRANSPORT OF DANGEROUS GOODS

# (OPERATIONS PERSONNEL INCLUDING CREW MEMBERS)

### 2.4.1	Approval of Dangerous Goods Training Programmes (JAR-OPS 3.1220(a))

Insert Text [‘Operator XXX’] hold approval for training programmes in the carriage of dangerous goods by air in accordance with JAR-OPS 3.1220(a). This training is identified and described in the following text. Any substantive changes to this training (or proposals for sourcing training from an alternative external company) must be submitted to the Dangerous Goods Office of the CAA for the training approval to remain valid.

Editorial Note: Prior to outsourcing the provision of dangerous goods training, operators must establish that the proposed training materials are approved by the CAA.

### 2.4.2	General Requirements Applicable to Dangerous Goods Training Programmes

To ensure that everyone involved is aware of their responsibilities in the transport of dangerous goods, no matter whether such goods are carried as cargo or are in the possession of passengers, training must be given so that an awareness is gained of the hazards associated with dangerous goods and how they should be dealt with in air transport.  Personnel identified in the categories specified in Table 1-4 of the ICAO Technical Instructions (extract produced below) must be trained or training must be verified prior to the person performing any duty specified in Table 1-4.

Training must be provided or verified upon the employment of personnel. Recurrent training must be provided within 24 months of previous training to ensure knowledge is current. However, if recurrent training is completed within the final three months of validity of previous training, the period of validity extends from the date on which the recurrent training was completed until 24 months from the expiry date of that previous training.

As with other aviation qualifications the expiry date of dangerous goods training is absolute and an offence against the regulations will be committed if staff continue to work after their training qualification has expired.

Editorial Note: Operators with a policy to provide recurrent dangerous goods training at periods of less than 24 months should state that policy.

A test to verify understanding must be undertaken following training and confirmation that the test has been completed satisfactorily is required. The records of training must be retained by the employer for a minimum period of 36 months from the most recent training completion date and must be made available upon request to the employee or the appropriate national authority.

### 2.4.3	Dangerous Goods Training Syllabus

The areas to be covered for various categories of personnel are listed within the table below; the depth of training required for each area is dependent on the responsibilities of the individuals and varies from a general appreciation to in-depth knowledge so that decisions can be taken.

Editorial Note: The following table should be tailored to match the categories of personnel employed by the operator.

Extract from Table 1-4 of the ICAO Technical Instructions (Content of Training Courses)

| Aspects of transport of dangerous goods by air with which they should be familiar, as a minimum | 1 | 2 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| General philosophy | X | X | X | X | X | X | X | X | X |
| Limitations | X |  | X | X | X | X | X | X | X |
| General requirements for shippers | X |  | X |  |  |  |  |  |  |
| Classification | X | X | X |  |  |  |  |  | X |
| List of dangerous goods | X | X | X |  |  |  | X |  |  |
| Packing requirements | X | X | X |  |  |  |  |  |  |
| Labelling and marking | X | X | X | X | X | X | X | X | X |
| Dangerous goods transport document and other relevant documentation | X |  | X | X |  |  |  |  |  |
| Acceptance procedures |  |  | X |  |  |  |  |  |  |
| Recognition of undeclared dangerous goods | X | X | X | X | X | X | X | X | X |
| Storage and loading procedures |  |  | X |  | X |  | X |  |  |
| Pilots’ notification |  |  | X |  | X |  | X |  |  |
| Provisions for passengers and crew | X | X | X | X | X | X | X | X | X |
| Emergency procedures | X | X | X | X | X | X | X | X | X |

KEY:

1	-	Shippers and persons undertaking the responsibilities of shippers.

2	-	Packers.

6 	-	Operator’s staff accepting dangerous goods.

7 	- 	Operator’s staff accepting cargo, mail or stores (other than dangerous goods).

8 	- 	Operator’s staff involved in the handling, storage and loading of cargo, mail or stores and baggage.

9 	- 	Passenger-handling staff.

10	-	Flight crew members and load planners.

11	-	Crew members (other than flight crew members).

12	-	Security staff.

Note 1:	Depending on the responsibilities of the person, the aspects of training to be covered may vary from those shown in the table.

Note 2:	The categories of personnel identified in Table 1-4 of the ICAO Technical Instructions (Content of Training Courses) are not all-encompassing. Personnel employed by or interacting with the aviation industry in areas such as passenger and cargo reservation centres, and engineering and maintenance, except when acting in a capacity identified in Table 1-4, should be provided with dangerous goods training commensurate with their specific responsibilities. See ICAO Technical Instructions 4;2.1.

### 2.4.4	Instructor Qualifications

Instructors of initial and recurrent dangerous goods training programmes must have adequate instructional skills and have successfully completed a dangerous goods training programme in the applicable category, or Category 6 of Table 1-4 of the Technical Instructions (applicable to operator’s staff accepting dangerous goods), prior to delivering such a dangerous goods training programme.

Instructors delivering initial and recurrent dangerous goods training programmes must at least every 24 months deliver such courses, or in the absence of this attend recurrent training.

Editorial Note 1: In addition to the above, Operators should detail the experience and aptitudes considered appropriate for the selection of trainers.

Editorial Note 2: The above section does not apply to the exclusive use of Computer-Based Training (CBT) and other self-study materials for the delivery of dangerous goods training, i.e. where none of the training is delivered in person. There must, however, exist adequate means to ensure that persons creating and maintaining self-study training materials are competent and their knowledge of the transport of dangerous goods by air remains current.

### 2.4.5	Identification of Training and Testing Materials

Editorial Note 1: Operators should detail the dangerous goods training and testing materials that have been subjected to approval for each category of personnel, so that they may be readily identified by trainers. The titles and revision numbers of presentations, videos, study books, handouts, visual aids and tests to verify understanding should be included. Additionally, the mark required to achieve a pass and procedures to be applied in the event that personnel do not achieve or maintain the required standards must be established. If preferred, reference may be made to a separate controlled document where this information is maintained.

Editorial Note 2: Tests to verify understanding must be conducted in a controlled environment that prevents collaboration.

2.4.6	Further information concerning training can be found in CAP 483: Training in the Safe Transport of Dangerous Goods by Air (Part A).

# Text boxes

5.2