This code induction door lock adopts the most advanced capacitive touch button, sensor card, stable performance, powerful function, easy to use. Passwords and sensor CARDS are all removed and prepared by users themselves to minimize security holes. The door lock is suitable for modern office, office building, apartment, villa, etc.

Main features:

The password keyboard and swipe area will lock up for 5 minutes for security reasons.

Door lock setting includes: configuration operation, delete operation, change password, volume adjustment, gao 'an

Full mode, time setting, open record query. The specific steps are as follows:

1. Menu operation

1) : press the initial key to loosen | -- - please enter the management password "0123456789 #" (the factory default password) |-1 configuration operation | -- -2 delete operation | -- -3 change password | -- -4 volume adjustment | -- -5 high security mode | -- -6 time setting

| - - 7 opens for record enquiries

1. Configuration operation (password)

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "1" button, voice prompt: "the current assigned sequence number is 1, please enter key" | -- - we enter "6 to 10 password Numbers to end with # #."

| - voice prompt "please enter the new password" | - "we enter" 6 to 10 password Numbers to end with # #."

| - - voice prompt configuration is successful, repeat the configuration please press the * button "| - - except * button to exit the operation menu by pressing any key

2. Configuration operation (card)

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "1" button, voice prompt: "the current assigned sequence number is 2, please enter key" | - we put "M1" in the credit card area.

| - - the voice prompt is "successful configuration, repeat configuration please press the * button" | - button to exit the operation menu by pressing any key other than *

3. Configuration operation (fingerprint)

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "1" button, voice prompt: "the current assigned sequence number is 3, please enter key" | - we put "fingerprint" in the fingerprint head.

| -- - voice prompt "please enter your fingerprint again" (finger does not need to be held in the fingerprint) | - - voice prompt "configured successfully, repeat configuration please press * key".

| - press any key to exit the operation menu

4: delete operation

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- -press the "2" button, voice prompt: "1 click the serial number to delete the password 3, delete the password 3, delete the card 4 all delete" | -- - press the corresponding numeric key voice prompt "delete the success, the menu has quit"

| - (if the lock plate with the fingerprint head is used to clear the fingerprint, 5 delete all (the total deletion is including the configured password, fingerprint, card, all will be cleared))

5: change the password

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "3" button, voice prompt: "please enter the original password" | - we enter the original password to be changed to end with the # key

| - voice prompt "please enter the new password" | - "we enter" six to 10 password Numbers to end with # #."

| - - voice prompt, please enter the new password again "| -" - we will again type "6 to 10 password Numbers to end with # #."

| - - voice prompt password change successfully, menu has quit"

6: volume adjustment

1) loosen the initial key

| -- - please enter the management password "0123456789 #" (factory default password) | -- - press "4" button, voice prompt: "1 low, 2 middle, 3 high"

| -- - press the corresponding digital key voice prompt "setting success, the menu has quit"

7: high security mode

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| - press "5" key, voice prompt: "1 in high security mode, 2 cancel high security mode" | - by pressing the corresponding number key voice prompt "has been into (or cancel high security mode), have withdrawn from the menu"

(high security mode: two different user keys (key includes: fingerprint, password, card) can be opened

8: time setting

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "6" button, voice prompt: "please enter 4 years"

| - we enter "2013" voice prompt "please enter 2 months"

| - we input "05" voice "please enter the two day" | - we input "05" voice "please input two"

| - we input "05" voice prompt "please enter 2 bits" | - - voice prompt "current time is 05, 05 May 2013, the menu has quit".

Open the door and record the query

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| - according to the "7" number keys, voice prompt: "the latest password to open the door to open the door to record is the serial number 1 management when the time is in May 2015, 05, head of the view on a press * key, check the next record, please press # #" | - press the corresponding number key voice "accordingly suggests" we check the record for a maximum of 200

5. Initialization

To lock circuit board power cuts, with the hand holding the circuit board on the initialize button, to the circuit board connected to 6 v direct current, until at the sound of a drip, press 4 let go again, voice prompt for "initializing, initial success"

: delete operation

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- -press the "2" button, voice prompt: "1 click the serial number to delete the password 3, delete the password 3, delete the card 4 all delete" | -- - press the corresponding numeric key voice prompt "delete the success, the menu has quit"

| - (if the lock plate with the fingerprint head is used to clear the fingerprint, 5 delete all (the total deletion is including the configured password, fingerprint, card, all will be cleared))

5: change the password

1) : press the initial key to release

| -- - please enter the management password "0123456789 #" (factory default password)

| -- - press "3" button, voice prompt: "please enter the original password" | - we enter the original password to be changed to end with the # key

| - voice prompt "please enter the new password" | - "we enter" six to 10 password Numbers to end with # #."

| - - voice prompt, please enter the new password again "| -" - we will again type "6 to 10 password Numbers to end with # #."

| - - voice prompt password change successfully, menu has quit"

6: volume adjustment

1) loosen the initial key

| -- - please enter the management password "0123456789 #" (factory default password) | -- - press "4" button, voice prompt: "1 low, 2 middle, 3 high"

| -- - press the corresponding digital key voice prompt "setting success, the menu has quit"