# 3 PART SPECIFICATION

PRODUCT NAME	 TSH SERIES TOUCH SENSE HANDLE

| PART 1 |  |
| --- | --- |
| System Description Basic use Limitations | The Securitron Magnalock Corporation Touch Sense Handle is sized to cover up existing mounting holes used for standard pulls on aluminum doors. It is employed to open inswinging doors or as an alternate push-open device for outswinging doors which provides a different look on aluminum frame glass doors. The Touch Sense Handle includes two legend plaques which state PULL or PUSH and which may be reversed to show a black or a silver finish. The unit has a double pole relay output. The NC contacts are wired to directly break power to the magnetic lock when the unit is touched. The NO contacts connect to the REX (request to exit) terminals in the access system controller so that no alarm event is created during free egress. In the event of a failure in the access control system, the Touch Handle will still directly release the lock. An electronic option called out by adding the suffix "T" to the part number adds a three second trailing edge time delay which keeps the door released for three seconds after the unit is no longer being touches. |
| References | ISO 9001 UL FWAX.SA6635 UL ALVY.BP7041 ULC FWAX7.SA6635 ULC UEHX7.BP7041 |
| Warranty | SECURITRON MAGNALOCK CORPORATION warrants that it will replace at customer’s request, at any time for any reason, products manufactured and branded by SECURITRON. SECURITRON will use its best efforts to ship a replacement product by next day air freight at no cost to the customer within 24 hours of SECURITRON’s receipt of the product from customer. If the customer has an account with SECURITRON or a valid credit card, the customer may order an advance replacement product, whereby SECURITRON will charge the customer’s account for the price of the product plus next day air freight, and will credit back to the customer the full amount of the charge, including outbound freight, upon SECURITRON’s receipt of the original product from the customer. SECURITRON’s sole and exclusive liability, and customer’s sole remedy, is limited to the replacement of the SECURITRON product when delivered to SECURITRON’s facility (freight and insurance charges prepaid by customer). The replacement, at SECURITRON’s sole option, may be the identical item or a newer unit which serves as a functional replacement. In the event that the product type has become obsolete in SECURITRON’s product line, this MAGNACARE warranty will not apply. This MAGNACARE warranty also does not apply to custom, built to order, or non-catalog items, items made by others (such as batteries), returns for payment, distributor stock reductions, returns seeking replacement with anything other than the identical product, or products installed outside of the United States or Canada. This MAGNACARE warranty also does not apply to removal or installation costs. SECURITRON will not be liable to the purchaser, the customer or anyone else for incidental or consequential damages arising from any defect in, or malfunction of, its products. SECURITRON does not assume any responsibility for damage or injury to person or property due to improper care, storage, handling, abuse, misuse, or an act of God. EXCEPT AS STATED ABOVE, SECURITRON MAKES NO WARRANTIES, EITHER EXPRESS OR IMPLIED, AS TO ANY MATTER WHATSOEVER, INCLUDING WITHOUT LIMITATION THE CONDITION OF ITS PRODUCTS, THEIR MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. |
| PART 2 |  |
| Manufactured Units Composition Materials | Replacement for any pull device on an inswing door. Activates a DP/ST 1Amp rated relay when touched (no mechanical movement) which will allow free egress. A backup push button, 16 ft. of 20AWG 6 conductor cable and a Stainless Steel - 630/US32D armored door cord included with the handle. Operates on either 12 or 24 VAC or VDC. |
| Accessories | Dummy TSB-3CL (w/o sensor, door cord, cable) Dummy TSB-3BK (w/o sensor, door cord, cable) TSB-3 Aluminum Bar Material — Clear Aluminum 48 Inch TSB-3 Aluminum Bar Material — Black Aluminum 48 Inch TSB-3 Mounting Base and Cap Assembly Mounting brackets used when replacing Jackson type mechanical bars. Black or Clear aluminum finish. Replacement sensor for TSB-3 Replacement 16 ft. cable with connector |
| Finishes | Clear anodized aluminum - 628/US28 or Black anodized aluminum - 335 finish. |
| PART 3 |  |
| Installation | Please refer to instruction manual (Securitron part number: 500-17700) Instruction manual can also be found on our website: www.securitron.com |

### EXIT DEVICE TSH-CL:

The Touch Sense Handle shall be produced by an ISO 9001 certified manufacturer.  The exit device shall employ an anodized aluminum finish and is intended to be a direct replacement  for any pull device on an inswing door. It shall activate a DP/ST 1Amp rated relay when touched (no mechanical movement) which will allow free egress.  A backup push button, 16’ ft. of 20AWG 6 conductor cable and a Stainless Steel - 630/US32D armored door cord shall be included with the handle. The device shall operate on either 12 or 24 VAC or VDC

Securitron model TSH-CL (TSH-BK) touch sense pull.

Rev 11-15-01

# Text boxes

SECURITRON SPECIFICATION

TSH SERIES TOUCH SENSE HANDLE