# 3 PART SPECIFICATION

##### PRODUCT NAME	  DK-16 SERIES KEYPAD

| PART 1 |  |
| --- | --- |
| System Description Basic use Limitations | The Securitron Magnalock Corporation DK-16 Series Keypad is an indoor single gang type digital keypad system designed for medium/high security control of electric locks. It consists of two components: the keypad and the CPU board connected by a 16 ft. cable. This allows the CPU board to be mounted within the protected area for higher security. Tampering with or even destroying the keypad will not release the door. The rugged Stainless Steel - 630/US32D keypad may be mounted outdoors in any environment as it is fully weatherproof. The keypad features true 10 digit operation (keys are not paired), three LEDs and a beeper. |
| References | ISO 9001. |
| Warranty Warranty Continued | SECURITRON MAGNALOCK CORPORATION warrants that it will replace at customer’s request, at any time for any reason, products manufactured and branded by SECURITRON. SECURITRON will use its best efforts to ship a replacement product by next day air freight at no cost to the customer within 24 hours of SECURITRON’s receipt of the product from customer. If the customer has an account with SECURITRON or a valid credit card, the customer may order an advance replacement product, whereby SECURITRON will charge the customer’s account for the price of the product plus next day air freight, and will credit back to the customer the full amount of the charge, including outbound freight, upon SECURITRON’s receipt of the original product from the customer. SECURITRON’s sole and exclusive liability, and customer’s sole remedy, is limited to the replacement of the SECURITRON product when delivered to SECURITRON’s facility (freight and insurance charges prepaid by customer). The replacement, at SECURITRON’s sole option, may be the identical item or a newer unit which serves as a functional replacement. In the event that the product type has become obsolete in SECURITRON’s product line, this MAGNACARE warranty will not apply. This MAGNACARE warranty also does not apply to custom, built to order, or non-catalog items, items made by others (such as batteries), returns for payment, distributor stock reductions, returns seeking replacement with anything other than the identical product, or products installed outside of the United States or Canada. This MAGNACARE warranty also does not apply to removal or installation costs. SECURITRON will not be liable to the purchaser, the customer or anyone else for incidental or consequential damages arising from any defect in, or malfunction of, its products. SECURITRON does not assume any responsibility for damage or injury to person or property due to improper care, storage, handling, abuse, misuse, or an act of God. EXCEPT AS STATED ABOVE, SECURITRON MAKES NO WARRANTIES, EITHER EXPRESS OR IMPLIED, AS TO ANY MATTER WHATSOEVER, INCLUDING WITHOUT LIMITATION THE CONDITION OF ITS PRODUCTS, THEIR MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. |
| PART 2 |  |
| Manufactured Units Composition Materials | Size: single gang Cable: 16 ft., 12 conductor, 22 gage Operating Environment: Indoor use. Visible/Audible Indicators: 3 LEDs and a beeper Construction: Cast Stainless Steel - 630/US32D with 12 keys (10 digits and * and # keys) Power: 12 to 24 volts AC or DC |
| Accessories | Spy shield. |
| Finishes | Satin Stainless Steel - 630/US32D plate, white keys with black lettering on a black surface. |
| PART 3 |  |
| Installation | Please refer to instruction manual (Securitron part number: 500-11300) Instruction manual can also be found on our website: www.securitron.com |

### Entry Device - DIGITAL KEYPAD SYSTEM - DK-16:

The Digital Keypad System shall be produced by an ISO 9001 certified manufacturer.  The Digital Keypad shall be of a telephone type with engraved and paint filled numbers in plastic keys suitable for mounting in a single gang box.  The Digital Keypad shall have a red a green and a yellow LED mounted on the face.  The Digital Keypad System circuit board shall be a remote unit to allow for increased security and shall operate on 12 or 24 volts AC or DC.  The Digital Keypad System circuit board shall be mounted in a metal enclosure and provide for multiple users.  It shall also have a DP/DT relay output for lock control and alarm shunt , camera call up or other device interface as well as a request to exit input.  The manufacturer shall provide a minimum of sixteen feet of cable to interface the Digital Keypad with its circuit board, and the system shall have user/installer programmable options such as anti - tailgate, anti - door prop, and duress code alarm.

Securitron model DK-16 digital keypad.

Entry Device - DIGITAL KEYPAD SYSTEM - DK-16W:

The Digital Keypad shall be of the single gang telephone keypad type with engraved and paint filled numbers in plastic keys.   The Digital Keypad shall be constructed of a durable plastic with a Stainless Steel - 630/US32D backplate.  The Digital Keypad System circuit board shall be a remote unit to allow for increased security and shall operate on 5 or 12 volts DC.  The Digital Keypad System circuit board shall interface with a PC based access system via  weigand data protocol. The manufacturer shall provide a minimum of sixteen feet of cable to interface the Digital Keypad with it’s circuit board.

Securitron model DK-16W digital keypad.

Rev 11-15-01

# Text boxes

SECURITRON SPECIFICATION

DK-16 SERIES KEYPAD