# Planar PT1910MX-Black 19” Resistive Touch Screen Monitor

| Planar – Manufacturer Part Number | Shipping Weight | Product Description: | Product description (shortened) | UPC Code | Model Number |
| --- | --- | --- | --- | --- | --- |
| 997-3985-00 | 25.8 lbs (11.73 kg) | 19” 5-wire resistive with dual serial/USB touch screen interface, -5 to 90º tilt range, side OSD button placement, black. | 19” resistive with dual serial/USB touch screen interface, -5 to 90º tilt range, black. | 8 10689 03985 3 | PT1910MX-BK |
| Overview: | The PT1910MX 19” touch screen monitor is perfect for use in healthcare, retail, point-of-sale and hospitality applications. Easily integrated with a variety of POS, thin client or PC systems, the monitor features a 5-wire resistive touch screen and dual serial/USB touch screen interface. Available in black or white, users may use a finger, gloved hand, credit card, pen or stylus to activate the resistive touch screen. The user can easily adjust the monitor from -5º to 90º based on preference. The OSD buttons are located on the side of the monitor to minimize setting changes. The OSD buttons can also be locked for customer-facing applications. It also comes with both analog and DVI-D input options. Planar has nearly 25 years experience delivering specialty display solutions for the most demanding applications. The PT products include Planar’s industry leading 3-Year Customer First™ Warranty featuring FREE 2-Day Advance Replacement. The result is an exceptional, cost-effective touch screen monitor. |
| Overview (shortened): | The PT1910MX 19” touch screen monitor is perfect for use in healthcare, retail, point-of-sale and hospitality applications. Easily integrated with a variety of POS, thin client or PC systems, the monitor features a 5-wire resistive touch screen and dual serial/USB touch screen interface. Users may use a finger, gloved hand, credit card, pen or stylus to activate the resistive touch screen. The user can also easily adjust the monitor from -5º to 90º based on preference. The OSD buttons are located on the side of the monitor to minimize setting changes. The OSD buttons can also be locked for customer-facing applications. It also comes with both analog and DVI-D input options. Planar has nearly 25 years experience delivering specialty display solutions for the most demanding applications. The PT products include Planar’s industry leading 3-year Customer First™ Warranty featuring FREE 2-Day Advance Replacement. The result is an exceptional, cost-effective touchscreen monitor. |
| Product Highlights: | Perfect for kiosk integrators, VARs and OEMs in healthcare, retail, POS or hospitality applications 19” size with SXGA resolution Economical 5-wire resistive touch screen Recognizes touch input from a finger, gloved hand, credit card, pen or stylus Dual serial/USB touch screen interface Solid, stable base with -5º to 90º tilt range Analog/DVI-D video input AC-DC dual power input for mounting flexibility OSD buttons on the side to minimize setting changes Compatible with mounting options that use the 75 / 100 mm VESA standard 3-Year Customer First™ Warranty featuring FREE 2-Day Advance Replacement |

Technical Specifications

| Description | Specification |
| --- | --- |
| Planar Part Number: | 997-3985-00 |
| Touch Screen Type: | 5-wire resistive |
| Touch Screen Interface: | Dual RS-232 serial/USB |
| Brightness w/Touch Screen (Typical): | 240 cd/m² |
| Brightness w/o Touch Screen (Typical): | 300 cd/m² |
| Compatibility: | Windows® VISTA, XP, 2000, ME, 98, CE, XP Embedded, Linux, Apple® Mac OS |
| Transmissivity: | 80%+ 2% |
| Contrast Ratio (Typical): | 800:1 |
| Response Time (Typical): | 5 ms (3.6 ms rise, 1.4 ms fall) |
| Viewing Angle: (Specified at CR>10:1) | 160º H, V |
| Pixel Pitch: | 0.294 |
| Refresh Rate: | 56-75 Hz |
| Input Options: | Analog, DVI-D |
| Power Supply: | Internal AC power supply 12V DC power connector (Optional DC power supply may be sourced separately) |
| Power Requirements: | 100-240 VAC |
| Power Consumption (stand by): | 50W (TBD) |
| External Connections: | D-sub 15-pin D-sub 9-pin DVI-D DC power connector Type B socket USB Stereo jack - 3mm |
| Audio – Built-in Speakers: | 2 speakers, 1W/ch |
| Features: | Anti-glare coating Multi-language support On screen display |
| Tilt: | -5º to 90º |
| Display Active Area: WxH | 19” diagonal |
| Native Resolution: | 1280 x 1024 |
| Dimensions w/stand (W X H X D): | 17.2” x 16.0” x 10.5” (438 mm x 405.5 mm x 266.2 mm) |
| Dimensions w/o stand (W X H X D): | 17.2” x 14.6” x 2.7” (438 mm x 370 mm x 68.6 mm) |
| Weight (w/stand): | 19.6lbs (8.9kg) (net) 25.8lbs (11.7kg) (shipping) |
| Weight (w/o stand): | 14.1 lbs (6.4 kg) |
| Approvals: | UL/c-UL , FCC-ClassB, TUV-T mark , CE, CB, RoHS |
| Service and Support/Warranty: | 3-Year Customer First™ Warranty featuring FREE 2-Day Advance Replacement (US only) |
| VESA Compatible/Location | Built-in 75/100 mm VESA, back |