July, 2001

BERRY TEST SETS

An Independent Technologies Company

# 312A-L2 and L3 TRUNK TEST SET

## Operator’s  Manual

Berry Test Sets, Inc.										             Berry Test Sets, Inc.

11640 Arbor Street    								                       Customer Service/Manufacturing

Suite 100							              					              26 First Avenue, SE

Omaha, NE  68144						       					      New London, MN  56273

402-498-8400					           		  					         320-354-5825

BERRY TEST SETS, INC. 									Issue 2, October 1994

Model 312A-L2 TRUNK TEST SET

and

Model 312A-L3 POSITIVE SLEEVE CURRENT ADAPTER

CONTENTS								  PAGE

1 .  GENERAL

A.  Scope of the Manual	1

B.  Applications	1

C.  Specifications	3

2.  DESCRIPTION

A. General	3

B. Physical Description	6

C. Front Panel	7

3.  OPERATION

A. General	9

B. MF Signaling System	9

C. DP Signaling System	9

D. Verification Tests	9

E. Circuit Testing	10

4.  MAINTENANCE

A.  Battery Use	21

B.  Battery Removal and Replacement	21

C.  Warranty Information	21

D.  Repairs	21

E.  Returned Material	21

FIGURES

1. 312A-L2 Trunk Test Set	5

2.  312A-L2 Front Panel	7

1A. 312A-L3 Adapter	5

2A. 312A-L3 Top Panel	8

TABLES

A. Terms, Abbreviations & Acronyms	3

B. Specifications	4

C. Sleeve Current Parameters	6

D.  MF Signaling System	9

E. Sleeve Resistance Values	11

F.  Ringing Voltage Requirements	19

1. 	GENERAL

A.	Scope of the Manual

1.01	This manual describes the features, operation, and maintenance of the Model 312A-L2 Trunk Test Set.  Application information and detailed testing procedures are also included.  A brief description of Multifrequency (MF) and Dial Pulse (DP) signaling systems are furnished as an aid to understanding and using the Model 312A-L2 Trunk Test Set.  It also describes the features and operation of the Model 312A-L3 Positive Sleeve Current Adapter.  Detailed testing procedures with and without the Model 312A-L3 Adapter are included.

1.02	This manual is reissued to add the Model 312A-L3 Positive Sleeve Current Adapter test features and test procedures.

1.03	 Terms, Abbreviations and Acronyms used in this publication are listed in Table A.

# B.	Applications

1.04	 The Model 312A-L2 Trunk Test Set is a portable Multifrequency (MF) and Dial Pulse (DP) sender with High-Low sleeve current control for testing 2-wire trunks arid trunk equipment It is used to furnish address and supervisory signals and provides a means to monitor and communicate on the trunk being tested

1.05	The Model 312A-L2 provides the following features:

-Access either MF or DP circuits Monitor tip and ring battery and ground on the ring

-Control sleeve current

-Access for external test sets

-Audio monitoring and communication over test trunks

- ON HOOK/OFF-HOOK control

1.06	The 312A-L2 furnishes an interface between the trunk being tested and the test equipment connected to it.  It also provides the necessary signaling and control features to access and signal a designated test number.  The 312A-L2 may be used to test:

-No Test Trunk circuits

-Main Distributing Frame Test Trunks (MDF)

-Test Trunk Ringing circuits (TTRC)

-Pair-Gain Test Controller circuits (PGTC)

-TOUCH-TONE Frequency Test  AppIique circuits (TTFA)

-Automatic Intercept Trunks (AIS)

-Inter and Intra Office Trunks

-Incoming arid Outgoing Trunk Equipment

-Incoming and Outgoing PBX Trunks

-CAMA Trunks

-TSPS Trunks

-Associated Trunk Facilities**

**When connected to a Loop Testing Frame (LTF) equipped with Mechanized Loop Testing (MLT-1) or Loop Testing

System (LTS) contained in (MLT-2).

1.07      A "Test Trunk" is any of the following:

* No-test trunk

* No test trunk circuit

* Incoming test trunk

* Test train

1.08      The Model 312A-L2 Trunk Test Set applications include:

* Test incoming trunks for reversal and completion

* Test incoming registers (MF and DP)

* Test outgoing trunks at the OGT frame

* Access "No Test" trunks

* Qualify "No Test" trunks for MLT application

1.09 	The Model 3l2A-L3 Adapter provides additional test features to enhance the testing capability of the Model 312A-	L2 Trunk Test Set. The L3 Adapter is required for the complete testing of MLT test trunks and associated 	control 	office trunks.

1.10    The Model 312A-L3 Adapter provides the following features:

-Positive sleeve current control switches.

-Applies battery to the tip and ring or positive battery to the tip of the test trunk,

-Conveniently connects to the Model 312A-L2 Trunk Test Set,

1.11    	The additional test applications available when using the Model 312A-L3 Adapter with the Model 312A-L2 Trunk 	Test Set are:

-A SLC-96 Channel Test.

-SXS Permanent Signal Release Test.

-Test Trunk Ringing Circuit Control.

-TOUCH-TONE Applique circuit tests (MLT-2 No Test Trunks only).

1.12	For MLT applications the Model 312A-L2 is functionally equivalent to the Western Electric

KS-22475 arid the Model 312A-L3 Adapter is equivalent to the Western Electric KS-22475 L2 Adapter

###### TABLE A

###### TERMS, ABBREVIATIONS AND ACRONYMS

AIS		Automatic Intercept System

CAMA		Centralized Automatic Message Accounting

CCITT		Consultative Committee on International Telegraph and Telephone

DE		Distribution Frame

DP		Dial Pulse

ERL		Echo Return Loss

IPM		Impulses Per Minute

LED		Light Emitting Diode

LTF		Loop Testing Frame

MDF		Main Distributing Frame

MLT		Mechanized Loop Testing

MF		Multifrequency

NMS		Noise Measuring Set

PGTC		Pair-Gain Test Controller Circuits

PPS		Pulses Per Second

TMS		Transmission Measuring Set

TN		Test Number

TRS		Tip (T)     Ring (R)       Sleeve (S)

TSP		Traffic Service Position

TSPS		Traffic Service Position System

TTRC		Test Trunk Ringing Circuit

C. Specifications

1.13	Specifications for the Model 3l2A-L2 Trunk Test Set are shown in Table B. The specifications for the

Model 312A-L3 Adapter are listed at the bottom of Table B.

2.	DESCRIPTION

# A. General

2.01 	The 312A-L2 Trunk Test Set furnishes MF (Multifrequency) and DP (Dial Pulse) address

signals for testing 2-wire trunks, trunk equipment and subscriber loops.   It also provides High-Low sleeve control and jack access for external test sets.  The 312A-L3 Adapter provides additional test capability to life 312A-L2 Trunk Test Set.

2.02	A photo of thee 312A-L2 is shown in Figure 1. The 312A-L2 is a portable test set with a carrying

strap attached and a test cord storage area in the cover of the set.  A photo of the 312A-L3 Adapter is shown in Figure 1A.  When not in use, the L 3 Adapter fits into the cover of the 312A-L2 Trunk Test Set.

2.03	The 312A-L2 may be powered from either an internal or external battery supply.  When it is powered from central office battery, -48 VDC is connected to the 48V 310 jack or the color coded BAT and GRD binding posts on the front panel.  If sleeve control is not required the set can be powered from a -24 VDC power source.  The POWER indicator LED will light when the set is energized.  An internal battery supply is provided for user convenience when central office battery is not available.  When the set is powered from its own battery supply it is energized when the CONTROL switch is in the OFF-HOOK position.  When the test set is not in use it should be turned off (ON-HOOK position) to conserve the batteries.  The sleeve current control function is not available when the set is being powered by its own batteries.

2.04	In the MF signaling mode, MF tones from the KEYPAD are generated in the standard 2 of 6 frequency format for digits 1 through 0, plus some special codes, that are listed in Table D. The MF frequencies are digitally generated from a crystal time base to insure long term accuracy and stability.  The rotary dial provides standard loop dial pulses at a rate of 10 pulses per second at 61.5% break.

2.05	There are two convenient methods available for connecting the trunk to be tested and external test sets to the 312A-L2.  Either the two parallel connected TRUNK jacks or the T, R and S binding posts may be used for this purpose.  The type of tests being made and the external test set used, will determine how these three access points are to be used.  This feature is useful in transmission and noise testing where the 312A-L2 is used to outpulse a test line number for a test tone, or quiet termination and the external test set is connected in parallel to make the measurements.

2.06	The 312A-L2 Trunk Test Set connection to the trunk being tested is made through the CONTROL switch.  With this switch in the OFF-HOOK position, the trunk is connected to the test set and loop current will be drawn if battery is present.  With the CONTROL switch in the ON HOOK position the test set is not connected to the trunk being tested.

TABLE B

## SPECIFICATIONS

2.07	Either the 312A-L2 or an external test set may provide a termination for the trunk being tested.  If a bridging type external test set is used, the 3l2A-L2 provides a 600 ohm termination with the CONTROL switch in the OFF-HOOK position.  If the external test set has its own built-in termination it then provides the termination necessary to hold-up the trunk being tested.  The CONTROL switch in this case should be placed in the ON-HOOK position after outpulsing to prevent a double termination on the trunk being tested,

2.08	Three front panel LED indicators designated BAT ON TIP, BAT ON RING and GRD ON RING display the trunk under test supervision status.  They provide a visual display of a sequence of alternating tip and ring signals occurring within a specific time duration that are used to convey address Information and call progress.

2.09    The SLEEVE CURRENT control circuit, in the 312A-L2, is a constant current sink that is connected to the sleeve

of the trunk being tested when the SLEEVE switch is in the CLOSED position.  Either a high or low sleeve current

value may be applied to the test trunk Table C lists the relevant cur rent flow parameters.

2.10	The 312A-L2 has headset jacks for plugging in a headset and communicating over the trunk being tested.  Monitoring on the trunk is also provided by a volume controlled amplifier and speaker.  It the headset used has an ON /OFF switch, the switch must be in the ON position in order to talk over the trunk under test.

TABLE C

## SLEEVE CURRENT PARAMETERS

CURRENT

SWITCH 		VALUE         	RMAX         	LED ON

LOW			14 mA		3200 Ohms	10 mA

HIGH			28 mA		1600 Ohms	20 mA

Note:	RMAX is the highest resistance for current to be within ±3%.

2.11  The Model 312A-L3 Adapter plugs directly into the tip, ring sleeve, battery and ground banana jacks of the 312A-L2

Trunk Test Set.  External devices may be connected to the color coded binding posts or they may be used to connect the -48 VDC office battery supply and the tip, ring and sleeve of the test trunk The test jacks, in the 312A-L2 Trunk Test Set, are wired in parallel with the binding posts, and may also be used for this purpose.

2.12	The 312A-L3 Adapter’s +CURRENT switch in the HIGH position provides a positive (+28 mA) and in the LOW position a positive ( + 14 mA) of constant sleeve current to the test trunk when the + SLEEVE switch is in the closed position.  The Adapter’s CURRENT LED will also light to show positive sleeve current flow.

2.13	Pushbutton (SLC) provides a positive (+) 116 VDC through 8K ohms of resistance to the tip side of the test trunk.  The Adapter also furnishes a 240 ohm battery source to the tip and ring of the test trunk.

B.	Physical Description

2.14	The 312A-L2 Trunk Test Set is a portable test set equipped with a carrying handle attached to a removable cover.  It has a ladder strap attachment for ladder use, and a built-in test cord storage area in the cover.  The test cords are not provided as a part of the test set.  Thee Model 312A-L2 Trunk Test Set is 6 inches high, 9 inches wide and 6 inches deep (1 5.2 X 22.9	X 15.2 centimeters).  It weighs 9 pounds (4.1 Kgs)

2.15	The 312A-L3 Adapter, when not in use, fits into the cover of the 312A-L2 Trunk Test set.  The Model 312A-L3 is 4.7 inches high, 5.5 inches wide and 1.2 inches deep, (11.9 X 13@9 X 3,0 cm ) and weighs 112 pound (23 Kg).

C. Front Panel

2.16	The front pane controls. indicators and jacks are shown in Figure 2. The circled callout numbers in the figure correspond with the circled callout numbers in the following text:

1	POWER red indicator lights when the test set's CONTROL switch is in the OFF-HOOK position and the internal battery supply is used. If	 the test set is being powered by -48 VDC, then the set is energized and the POWER indicator lights regardless of the position of the CONTROL switch.

Note: 	1 - The POWER indicator will not light if the internal batteries are low.

2 - Sleeve control is not available when the set is on its internal batteries.

2	BAT and GRD color coded binding posts for connecting central office battery to the test set.  The binding posts are wired in parallel with the -48V jack.

3	T, R and S color coded binding posts are a user convenience for connecting the trunk to be tested or other external test sets to the 312A-L2.  The three binding posts are wired in parallel with the two TRUNK jacks.

4	The two tip, ring and sleeve trunk jacks are wired in parallel with the T, R and S binding posts and provide access to the test set for the trunk to be tested and/or for external test sets.  Both jacks accept 310 type plugs and standard P2J or equivalent test cords.

5	The -48V jack accepts a 310 plug with a standard P2J or equivalent cord. It is used to connect the external -48 VDC power source to the test set.  The tip carries the (negative) battery and the sleeve the (positive) ground.

Note: 	1 - If the sleeve current function is not required, -24 VDC may be used (ESS office).

2 - A plug in the 48V jack disconnects the test set from its internal batteries.

6	The TEL SET jacks accept VVECO type 464A plugs and operate with a standard telephone handset or headset. including VVECO 52A, G3,  Plantronics Star Set. etc.

7	Screws at each side of the face panel that must be removed for internal battery maintenance.

8	Built in monitor speaker.

9	VOLUME control knob for adjusting the adjusting the speaker amplifier to the desired level.  Maximum gain is full clockwise.

10	The C0NTR0L  0N-H00K/0FF-H00K switch connects the internal tip and ring of the test set to the trunk being tested.  In the ON-HOOK position the test set is not connected. In the OFF-HOOK position the test set is connected to the test trunk and loop current is drawn if battery is present.

11	BAT ON TIP red indicator lights when the tip is more negative than the ring.

12	BAT ON RING red indicator lights when the ring is more negative than the tip.

13	GRD ON RING green indicator lights when a low resistance ground is on the ring (under 1500 ohms).

14	The SLEEVE switch in the CLOSED position connects a constant current source to the sleeve of the trunk being tested.  In the OPEN position the constant current source is disconnected.

15	The CURRENT switch provides 28mA of sleeve current in the HIGH position and 14mA in the LOW position.

16	CURRENT green indicator lights when either high or low sleeve current is flowing.  See Table C.

17	ROTARY DIAL for furnishing Dial Pulse (DP) address signals.

18	KEYPAD for selecting Multifrequency (MF) address signals.

19	STP - IDDD request for Directory Assistance Operator (code 12).

ST2P The same as KP1 except used for non-terminating IDDD calls.

ST3P - CAMA reset signal or IDDD request for Inward Assistance Operator (code 11).

20	ST - Indicates the end of MF pulsing.

21	KP1 - Indicates the beginning of the MF pulsing.

2.17	The top panel of the 312A-L3 Adapter is shown in figure 2A.  Call outs in the Figure correspond with call outs in the following text:

1	PS RLS pushbutton applies a 240 ohm battery to the tip and ring of the test trunk.

2	SLC pushbutton applies a positive (+) 116 VDC (through 8K ohms) to the top side of the test trunk with the ring 	side open.

3	T, R, S, BAT and GRD binding posts for connecting 48 VDC office battery and the test trunk or external devices.  	They are wired in parallel with the 312A-L2 Trunk Test Set’s similar binding posts and test jacks.

Note:  The T. R. S, BAT and GRD plugs at the bottom of the Adapter plug into the similar designated binding posts on the 312A-L2 Trunk Test Set.

4	+SLEEVE switch when in the CLOSED position connects a constant positive (+) current source	to the sleeve of 	the test trunk.  It is removed when the switch is in the OPEN position.

5	+CURRENT switch selects either a HIGH (+ 28 mA) or LOW (+14 mA) constant sleeve current source.

6		+CURRENT LED is illuminated when either HIGH or LOW sleeve current is flowing.

3.	OPERATION

A.	General

3.01	This section provides instructions for using and operating the 3l2A L2 Trunk Test Set.  The operating procedures include a brief description of the tests.  Information on the two types of signaling modes employed by the 312A-L2 are also presented.

B.	MF Signaling System

3.02	The MF signaling method uses six frequencies in the voice frequency band.  A combination of two of the six frequencies represents a digit.  Ten tone combinations are used for the 10 numeric digits (0-9), one combination for the (ST) signal and another for the (KP) signal . The three remaining tone combinations are used to provide other special signals.  Refer to TABLE D.

3.03	On intertoll circuits, MF signaling is used to transmit the address information and SF signaling provides the circuit supervision signals.  For most MF systems the pulsing rate is between 58 and 75 milliseconds for the pulse and interdigital intervals, or about 7 to 10 digits per second.  MF signals are usual y transmitted at a -6 or -7 dB level below the circuit voice level.  Table D shows the digits and frequencies along with the control function performed by the special codes.

TABLE D

## MF SIGNALING SYSTEM

C.	DP Signaling Systems

3.04	A rotary dial transmits digital information by opening and closing the circuit, which is really a sequence of ON-HOOK/OFF-HOOK signals.  The numerical digit dialed is determined by the number of ON-HOOK intervals in the train of pulses.  Pulses are usually generated at a rate of 10 per second with a 58 to 64 percent break ratio.

D.	Verification Tests

3.05	The purpose of the following test procedure is to verify that the 312A-L2 Trunk Test Set is in good working order prior to any circuit testing.  Make the test by performing the following procedure steps:

1 .	For internal battery operation, operate the CONTROL switch to OFF-HOOK and the POWER indicator should light.  Restore the CONTROL switch to ON-HOOK.

Note: If central office -48 or -24 VDC battery is available proceed to step 2. If not. skip step 2, and start with step 3.

2.	For external battery operation, connect -48 or -24 VDC to the -48V jack.  Use a patch cord equipped with a 310 type plug with the battery on the tip and ground on the sleeve.  The POWER indicator should light when the plug is inserted into the -48V jack.

3.	At a working telephone set disconnect the telephone from the connecting block.  Connect the tip and ring on the connecting block to a TRUNK jack on the 3l2A L2.  Use a patch cord equipped with insulated clips on one end and a 310 plug on the other.

4.	Insert the 310 plug into a TRUNK jack on the 312A-L2

5.	Operate the SLEEVE switch to the OPEN position.

6.	Plug a headset into the TEL SET jacks.

7.	Operate the CONTROL switch to OFF-HOOK, note that BAT ON RING indicator lights.

8.	 Dial tone should be heard in the headset and also over the monitor speaker. The VOLUME control should be turned clockwise to increase the volume.

9.	Dial a known telephone number with the rotary dial

10.	Audible ringing should be heard.  When the called number answers, a talking path should now be established.

11.	Operate the CONTROL switch to ON-HOOK releasing the called telephone.  Disconnect the patch cord from the connecting block and reconnect the telephone set.  Remove the 310 plug from the TRUNK jack.

12.	The 312A-L2 should new be ready for use for trunk testing.

E.	Circuit Testing General

3.06	Circuit access for testing is easiest wherever test jacks are available. Some of the locations having jack access are:

-Outgoing Trunk Test Frame (OGT)

-Testboards

-Switchboards

-Central Office Equipment

3.07	Most test jacks of the type listed above are normaled through and the circuit will be opened when the jack is plugged into.  A monitor jack is bridged across the circuit, and in some cases isolating resistors are also provided.  Service on the circuit will not be interrupted when a monitor jack is used for test access.

3.08	The No Test Trunk Circuit tests are used to check the operability of the test trunk circuits.  All circuits should be tested.  The tests are best performed at the trunk circuit where the circuit operation can be watched.  The 312A-L2 Trunk Test Set can be connected directly to the T, R, and S of the trunk circuit at the equipment location jacks or at the MDF.

3.09	Nearly all tests made with the 312A-L2 Trunk Test Set require a dial-up test termination.  Test terminations are provided in nearly all offices and in many PBX’s.  The most frequently used in Toll Offices are:

-100	Balance Test Termination

-102	1004Hz Milliwatt Test Tone

-103	Reverse Battery Supervision Signals

These same test terminations appear in many local central offices and PBXs where they are assigned standard 7 digit telephone numbers.

3.10	The following test procedures are used for testing circuits or equipment using either MF or DP signaling systems.

Setup Procedures

3.11	The following describes how battery and ground and the trunk to be tested (T, R and S) are connected to the 312A-L2 Trunk Test Set.  Before accessing a circuit for test, the following steps must be performed:

1.	Connect battery and ground to the test sets -48V jack with a standard P2J or equivalent cord.  The POWER indicator should light.

2.	If internal batteries are used. operate the CONTROL switch to OFF-HOOK and the POWER indicator should light.  Restore CONTROL switch to ON-HOOK.  The SLEEVE control function is not available when using the internal battery supply.

3.	Verify that the following switches are positioned as indicated:

Switch		Position

CONTROL	ON-HOOK

SLEEVE	CLOSED

CURRENT	HIGH*

*Note, Some offices may require the LOW position.

SLEEVE RESISTANCE - Assuming a distant end connection of the SLEEVE to CO GRD, the 312A-L2 power source to be CO GRD and -48 VDC, and the sleeve is connected to the set either by the TRUNK jack or "S" binding post; the 312A-L2 can be used to estimate the value of the sleeve resistance.  The SLEEVE switch must be in the CLOSED position.  Table E lists the values.

TABLE E

# SLEEVE RESISTANCE VALUES

SWITCH	LED		R SLEEVE

LOW		OFF		4500 ohms

HIGH		OFF		2250 ohms

HIGH		ON		2250 ohms

Note: The values are accurate to ± 10%

4.	Connect the T, R and S of the test trunk to one of the TRUNK jacks with a P2B or equivalent cord.

3.12 	Whenever the 312A-L3 Adapter is used, make sure that the battery plug of the Adapter s connected to the battery jack of the 312A-L2 Trunk Test Set.

Note:	Use the T, R S BAT and GRD binding posts on the 312A-L3 Adapter whenever external devices are required.

3.13	If a series of tests are to be performed on a number of circuits, these initial set-up procedures must always be established prior to connecting another circuit to the 312A-L2

C.	Circuit Testing Procedures

3.14	The following instructions cover the connections and operation of the 312A-L2 Trunk Test Set

for typical circuit tests:

(a)	Test Procedure 1: Covers the accessing of any test line used for No Test Trunks.  The set-up procedures

outlined in this procedure cover most No Test Trunks.

(b)	Test Procedure 2: Covers the Tone Access Test - 120 IPM,

(c)	Test Procedure 3: Covers an Outgoing Trunk Test to a PBX.

(d)	Test Procedure 4: Covers the SXS Permanent Signal Release Test.

(e)	Test Procedure 5: Covers the SLC-96 Carrier System Channel Test.

(f) 	Test Procedure 6: Covers the Test Trunk Ringing Circuit.

(g)	Test Procedure 7: Covers the TOUCH-	TONE Dialing Pad Test.

Note:	Test Procedures 4. 5, 6, and 7 require the 312A-L3 Adapter,

## TEST PROCEDURE NO. 1

## Typical connecting arrangements for test No Test Trunks with the 312A-L2 Trunk Test Set

Notes:	Test 1. Used to test for proper circuit operation.  The Test Set is connected to the tip, ring and sleeve terminal

at the equipment.  This test arrangement may be used for new equipment and maintenance purposes.

Test 2. The Test Set is connected at the MDF.  This type of arrangement is used to check a I trunk circuits in the

office from one location without going to each circuit individually.

Test 3. The Test Set is connected to the MDF at the LTF location.  All Test Trunks connected to the LTF/ LTS can

be tested.  This configuration used when LTF is not equipped with Test Trunk jacks.

Test 4. The Test Set is  connected to the Jack Panel on the LTF/LTS.  This provides a convenient testing location

for all No-Test and MDF Trunks. (See Note below.)

Note:	The Test Set must be isolated from the LTF, i.e.,  T, R, S must be opened along with the G lead between the Test Set and the LTF.  This can be done by lifting the jumpers at the MDF.  If the G lead is returned to the LTF for grounding, then after it is opened a ground must be placed on the G lead toward the test trunk circuit, If a Test Jack Panel is used at the LTF it s not necessary to open the leads at the MDF.  It will be necessary to open the "S" screw (on the TAB) associated with the trunk under test.

## TEST PROCEDURE NO. 1

###### No Test Trunk testing procedure for operating the 312A-L2 Trunk Test Set

TEST PROCEDURE NO. 2

Tone Access Test.  For this test, the 120 Interruptions Per Minute (IPM) overflow feature of the test trunk is tested.

Note:  See Test Procedure No 1 for applications under which Test Locations 1, 2, 3 or 4 should be used.

#### TEST PROCEDURE NO. 2

TEST PROCEDURE NO. 3

### This procedure covers the test on a PBX trunk from an Outgoing Central Office Trunk Circuit.  A balance. (return loss) noise, or transmission test may be made with this test arrangement using External test equipment.

Note: If Trunk Circuit is equipped with jacks the Trunk Test Set should be connected at that point.  If it is not, then

the T, R and S should be opened at the Distribution Frame and the Trunk Test Set connected at that point.

### TEST PROCEDURE NO. 3

This test a from a Central Office Outgoing Trunk to a PBX. Tests for Transmission and Echo Return Loss are similar.

TEST PROCEDURE NO. 4

This test procedure covers the SXS Permanent Signal Release feature.  For this test the release from dial tone capability of the permanent signal release circuit will be tested (Test requires the 312A-L3 Adapter).

## TEST PROCEDURE NO. 4

# TEST PROCEDURE NO. 5

This test procedure covers the SLC-96 Carrier System Channel test.  For this test, the line from the accessed Test

Number to the SLC Carrier System Channel unit (in the SLC carrier system channel bank) will be tested, (the test

requires the 312A-L3 Adapter).

Note: 	Test 1.  Refer to Test Procedure No I for connecting arrangements to use if test is made with CO test

trunk circuit.

Test 2.  Test may also be made by connecting the Test Set directly to the PGTC of the SLC 96.

# TEST PROCEDURE NO. 5

## TEST PROCEDURE NO. 5 (Continued)

###### TEST PROCEDURE NO. 6

This test procedure covers the Test Trunk Ringing Circuit test.  For this test, the test trunk ringing circuit (TTRC) associated with the MLT-2 or no-test trunk will be activated.  he ringing and trip capabilities of the TTRC are also tested. (Test requires the 312A-L3 Adapter).

#### TEST PROCEDURE NO. 6

## TABLE F

TEST REQUIREMENTS FOR RINGING VOLTAGES

###### TEST PROCEDURE NO. 7

This test procedure covers the TOUGH-TONE Dialing Pad Test (MLT-2 No Test Trunks Only).  For this test, the TOUCHTONE frequency test applique (TTFA) circuit (electromechanical switches) or the TOUCH TONE (dialing test

circuitry (in ESS switches) will be activated (Test requires the 312A-L3 Adapter).

TEST PROCEDURE NO. 7

4.	MAINTENANCE

A.	Battery Use

4.01	The 312A-L2 Trunk Test Set is shipped with premium alkaline D cells for long life and reliable operation.  Battery life depends on the test set use and it is possible, depending on use, for them to provide a year or more of service.  Always turn the test set off (ON-HOOK) when not is use.  The (POWER) indicator will not light when the batteries are weak.

4.02	The batteries can be replaced with any D type cell.  However, Berry Test Sets recommends Eveready No. E95 alkaline D cells for long life and leak-proof construction.

B.	Battery Removal and Replacement

4.03	To remove and replace the batteries it is necessary to remove the four front panel screws shown in Figure 2. Next step is to lift the front panel and electronics package from the case.  If the rubber gasket is tight, a small screwdriver may help loosen it, Lay the front panel and electronics package down and locate the battery hold-down plate.  Remove the four screws holding the plate and remove it.  Remove the old batteries and install the replacements.	(Correct polarity and battery direction is shown on the battery holder.) Reassemble the test set,

C.	Warranty Information

4.04 	Complete warranty information is contained in the purchase order agreement under terms and conditions of sale.  Summarized briefly, all Berry Test Sets, Inc. products are warranted against defects in materials and workmanship for one year from the date of shipment.

D. Repairs

4.05	Any Berry Test Sets product found to be defective must follow this procedure:

A)	Call and request a Return Transaction Authorization number (RTA) from Customer Service in New London, MN;

320-354-5825, or Omaha, NE at 402-498-8400.

B)	Provide a P.O. Number or Credit Card for billing, unless the set is in warranty.

C)	Display the RTA number on the outside of the shipping carton, and all accompanying paper work.

D)	Include a brief description of the nature of the problem.

Berry Test Sets products covered under terms of the above specified warranty will be repaired or replaced at Berry Test Sets' expense.  All other repairs will be at the customer's expense.  Charges are based on a flat rate schedule.

E.	Returned Material

4.06	Whenever possible, Berry Test Sets, Inc. products being returned for repair should be shipped in the original shipping carton.  All instruments must be shipped to the following address:

BERRY TEST SETS, INC.

26 First Avenue, S.E.

New London, MN 56273

Attn: Repairs

4.07	Equipment (in or out of warranty) when shipped by air freight will be repaired within four working days and reshipped air freight.  Equipment received by surface freight will be repaired within 10 working days.

# Text boxes

Independent Technologies/Berry Test Sets

11640 Arbor Street

Suite 100

Omaha, NE  68144

402-496-4700/402-498-8400

www.independenttech.com

www.berrytestsets.com