| Item Qty. | 2-channel week time switch REG 371 |
| --- | --- |
| Design: DIN rail mounted device. Dimensions: DIN rail dimensions, 2 modules wide (1 module = 18 mm). The 2-channel week time switch REG 371 offers 36 switching times for instabus EIB. The 2-channel week time switch enables: temporary or continuous manual operation; automatic conversion of summertime/wintertime; sending of switching, priority control, dimming and value telegrams; 99 day holiday program, 99 days can be set in advance; cyclical sending of telegrams; one scene per channel with up to four different telegrams; retention of switching time settings for up to 10 years on voltage failure. 7 buttons for setting the day of the week, hour, minute, time, programming input and 4 manual operations. LCD display for time, weekday, summertime/wintertime, holiday program, switching state of the 2 channels, manual operation. During the configuration of the 2-channel week time switch, the installer must carry out all the necessary settings. Nominal voltage: DC 29V. Bus connection: via bus terminal |

Manufacturer: Siemens Order no.: 5WG1 371-5EY01

| Supply, install, assign parameters, label, |
| --- |
| commission and document |
| Material:.......... | Labour:.........….... |
|  | EP:..............…...... | GP:..................... |