ENGINEERING DOCUMENT

757-4002-097		CAD #D8478

SUBJECT: Siemens I/R Module, Servo Drive, and Spindle Drive Setup

Procedure with Ultimax 3 ISA Control.  Applicable Machining Centers:

BMC30M, BMC30HT, BMC30SSM, BMC4020HT and BMC4020SSM.

RECORD OF CHANGES

Engineering Document 757-4002-097	CAD #D8478

| Revision | ECN # | Revision Description | Rev By | Date | Appd By | Date |
| --- | --- | --- | --- | --- | --- | --- |
| A | 13709 | Original Release |  |  |  |  |
| B | 13760 | Change P-31 = 15, P-146 = -500, and P-242 = 6 | DEO | 7/23/96 | MFC | 7/30/96 |
| C | 13933 | 1) Page 7, section VII-E-4 was ...until the axis stops rotating. 2) Page 8, section VIII was ...FA0 for motor P/N. Section X added Z=opt. 3) Attachment “A” and Attachment “B” Page 1, P-027 was 20 RPM and Page 4, P-144 was 1.00 degree. 4) Added BMC30SSM. 5) Page 6, section VII-B-1, reworked “KP” adjustment procedure. | DEO | 12/16/96 | MFC | 12/17/96 |
| D | 14012 | 1) Page 9, section XII-A, BMC30’s Drive code Parameter added 13. 2) Page 11, section XIV-B4, Spindle RPM Range acceptability table was added. | SAW | 7/14/97 | DEO | 7/14/97 |
| E | 14098 | 1) Page 6, Revised “TN” adjustment procedure for fine-tuning. 2) Page 8, Added spindle motor option K03. 3) Page 13, section A1, parameter P1-149 was 29H (uni-directional). 4) Attachment “B” for BMC4020 machines, P-149 was 29H. | DEO | 9/16/97 |  |  |

I.	INTENT

To provide a standardized method of configuration and adjustment with Siemens I/R module, servo drives, and spindle drives being used on Ultimax 3 ISA type machining centers.

II.	APPLICABILITY

Specific to all BMC30M, 30HT, 4020HT, and 4020SSM Ultimax 3 type machining centers using software version 1.62 or later.  This is the only procedure to be used within Hurco facilities and should be used at customer installations to help achieve factory proven performance.

III.	INDEX

Page 3		I/R Module Startup Sequence

Page 5		ULTIMAX 3 Control Parameter Verification, Servo

Page 5 		Servo Drive Start-up Sequence

Page 6		Servo Drive Adjustments and Tuning

Page 8		Hurco/Siemens Part Identification Table, Servo

Page 8		ULTIMAX 3 Control Parameter Verification, Spindle
Page 8		Hurco/Siemens Part Identification Table, Spindle
Page 9		Spindle Start-up Sequence
Page 9		Identify Drive and Motor Type
Page 10	Parameter List, Manual Entry
Page 10	Spindle Zero RPM and Maximum RPM Calibration
Page 12	Orient Zero Mark Setup with Motor Encoder
Page 13	Orient Zero Mark Setup with Motor Encoder & Proximity Sensor
Page 15	Re-initialize Spindle Drive
Attachment A	Siemens Spindle Parameter List, BMC30HT & BMC30M
Attachment B	Siemens Spindle Parameter List, BMC4020HT & BMC4020SSM

IV.	I/R MODULE START-UP SEQUENCE

CAUTION:  During this procedure high voltage will be present once the I/R module has been powered up.  It will take approximately 5 minutes to discharge when power is removed.  Begin sequence with control power turned OFF.  Do not disconnect or reconnect wires or connections unless power is OFF and the DC link has discharged.

A.	Remove all external interface wiring (X161 and X121), the DC link connections, as well as signal ribbon cables.  This isolates the module from the effects of possible problems from other modules and any other external wiring errors.

B.	Visually check to make sure that all I/O, ribbon, and power cables are securely terminated at the proper locations.  Also verify that the 600VDC bus bar links are securely terminated.  They are located behind a plastic protective front cover.

C.	Verify configuration of dip switch S1, access located through top of the module case.  Configure the module to indicate “fault” when applicable.  The internal relay will energize if power is ON and no fault is present.  Switch settings are as follows:

| S1-1 | OFF |
| --- | --- |
| S1-2 | ON |
| S1-3 | OFF |
| S1-4 | OFF |
| S1-5 | OFF |
| S1-6 | OFF |

D.	Apply main power to terminal at location U1, V1, and W1 via CB4 (32A).  Measure line voltage across each phase, it should be 380VAC to 420VAC (Reading may be as high as 440VAC which is acceptable when there is a no load condition).  No LED’s will illuminate at this time.

E.	Reinstall external wiring connectors at X161 and X121.  This will prepare the module for power-up operation.

F.	Reapply three phase main power via CB4 (32A).  This will verify that the module is functioning properly.  The DC link will be enabled and the green and yellow LED’s will illuminate.  The red fault LED should remain extinguished.

G1 - Unit Not Ready
Y1 - Unit Ready
R1 - +/- 15V Too Low
R2 - Supply Undervoltage, Phase Failure,
	 - or Control Axis Fault
R3 - 5V Too Low
R4 - DC Link Voltage Too High

G.	Verify low voltage power supply is functioning properly by measuring the following test points with respect to ground (X141-15).

| X141-7 | 24 +/- 1 VDC |
| --- | --- |
| X141-45 | 15 +/- 0.5 VDC |
| X141-44 | -15 +/- 0.5 VDC |
| X141-10 | -24 +/- 1 VDC |

H.	Enable control power from the ULTIMAX Control by selecting MANUAL Mode; F7 (“Reset Servos and Spindle”); depress <POWER ON>.  At this point the Drive Enable signal is enabled and DC link voltage is present at the bus.  The green LED will be extinguished and the yellow LED will remain illuminated.  At this point the I/R Module is considered operational.

V.	ULTIMAX 3 CONTROL PARAMETERS VERIFICATION, SERVO

Load parameters from the latest Engineering Document published to date (757-4002-048) per machine type.

A.	On the Ultimax Control select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F7 (“ATC and Machine Diagnostics”); <ENTER>, 103, <ENTER>.

B.	Select each axis softkey to review and/or load the Axis Tuning Parameters.

C.	If an Axis Parameter needs to be changed then simply enter the correct values per the referenced Engineering Document.

D.	After completing all changes for an axis, select the BEGIN TUNE softkey followed by the STORE PARAMETERS softkey.

E.	Press the EXIT softkey to return to the ATC & Machine Diagnostics screen.

F.	Press the Auxiliary mode key.

G.	Select the SYSTEM CONFIGURATION softkey.

H.	Insert the Machine Configuration diskette into the floppy drive.

I.	Select the BACKUP MACHINE CONFIGURATION softkey.

J.	When compete, remove the diskette from the floppy drive and store in safe location.

VI.	SERVO DRIVE START-UP SEQUENCE

CAUTION:  During this procedure high voltage will be present once the Servo modules have been powered up.  It will take approximately 5 minutes to discharge when power is removed.  Begin sequence with control power turned OFF.  Do not disconnect or reconnect wires or connections unless power is OFF and the DC link has discharged.  Also the following procedure requires that the I/R Module be operational as a prerequisite.  Bracket notation [ ] describes the second axis on a 2-axis module when applicable.

A.	Beginning with the leftmost module, isolate any module to the right by removing the ribbon harness, I/O, and the DC link connections.  This isolates the module from the effects of possible problems from other modules or any external wiring errors.

B.	Preset motor controller settings via internally located switches.  Remove the controller PCB front panel by loosening top and bottom captive screws.  Carefully pull the controller PCB assembly out of its module.  Preset the controller switches as follows:

| System | Switch S1 [S4] | Switch S2 [S5] | Switch S3 [S6] |
| --- | --- | --- | --- |
| BMC30M | ALL switch jumpers OPEN | Bits 1, 6, 9 ON Bits 2-5, 7, 8, 10 OFF | Bit 8 ON Bits 1-7 OFF |
| BMC30HT | ALL switch jumpers OPEN | Bits 1, 9 ON Bits 2-8, 10 OFF | Bit 8 ON Bits 1-7 OFF |
| BMC4020HT | ALL switch jumpers OPEN | Bits 1, 9 ON Bits 2-8, 10 OFF | Bit 8 ON Bits 1-7 OFF |
| BMC4020SSM | ALL switch jumpers OPEN | Bits 1, 9 ON Bits 2-8, 10 OFF | Bit 8 ON Bits 1-7 OFF |

Description

S1 [S4]		Tachometer Matching Switch

S2 [S5]	Bit 1	Motor Rotation Direction vs. Voltage polarity

Bits 2-5	Current Limit

Bits 6-9	Current Gain

Bit 10	Velocity Mode vs. Current Mode

S3 [S6]	Bits 1-7	Factory Default Settings

Bit 8	Current Controller Integrator Active

C.	Switch presetting for motor controller is complete.  Reinstall the controller PCB assembly into the module.  Be careful to align the assembly in the card guide and “seat” it firmly into the rear connector.  Re-secure the retaining screws at the top and bottom of the front panel.

VII.	SERVO DRIVE ADJUSTMENTS AND TUNING

A.	Visually check and make sure the ribbon harness, I/O, and the DC link connections are securely terminated at the proper locations for the module under test.

B.	Axis amplifier “Proportional Gain” adjustment.  This adjustment is used to best match the servo axis performance to the requirements of the machine and controller.

1.C5	Initially adjust the potentiometer labeled “KP” to 30-50% from zero in a clockwise direction.  Zero being the hardstop when rotating the potentiometer fully counter clockwise. Adjust “KP” until motor starts to oscillate, then back off until it stops.  After it stops, turn the pot slightly 10% counter clockwise (25% is typically a good final setting for this adjustment).

C. E1	Axis amplifier “Integral Gain” adjustment.  This adjustment is used to best match the servo axis performance to the requirements of the machine and controller.

- Adjust the potentiometer labeled “TN”, to approximately 70% from zero in a clockwise

direction.  Zero being the hardstop when rotating the potentiometer fully counter

clockwise.

- Connect a digital voltmeter (DVM) to drive test point “W” (positive lead) and test point

“M” (common) for specific axis under adjustment.

3.        Program the given axis to move back and forth at 50 IPM and observe the stability of

speed regulator current expressed as a voltage.

4.        Fine adjust the “Integral Gain Adjustment” potentiometer labeled “TN” until the

voltage measured at drive test points becomes stable (typically +/-10mV fluctuation is

adequate).

D.	The “AD” potentiometer serve the purpose of “Low Speed Adaption” which is non-functional in our application because we are not setting S3 [S5] bit 5 ON.  Therefore just leave this potentiometer at the factory default setting.

E.	Axis amplifier “Drift” adjustment.  This adjustment minimizes motor rotation when a 0V command is issued in velocity loop.  Do not adjust the VR potentiometer on the MX4 board!  Leave them at their factory setting.  The range of adjustment available from the Siemens Servo modules is sufficient to balance servo offset.

1.	On the ULTIMAX Control select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F7 (“ATC and Machine Diagnostics”); <ENTER>, 101, <ENTER>; F6 (“Toggle Following Error Display”); F7 (“Axis Balance Adjust”).

2.	Select the appropriate softkey to choose the axis to be balanced.

3.	At the prompt, press the START push-button, followed immediately by pressing MOTION HOLD to provide a zero voltage signal from the selected MX4 DAC channel.  (The machine control loop is now open for this channel.  The presence of system unbalance will be immediately apparent by the drift of the values in the Following Error display).

4. C1	Adjust the uppermost potentiometer labeled “DRIFT” to minimize axis rotation.  In this mode it is impossible to guarantee no rotation.  Verify the quality of the null by observing minimal change in the counts being displayed in the Standing (Zero Speed) Following Error column.

F.	Axis amplifier “Tachometer” adjustment.  This adjustment is used in the velocity loop and made to scale the motor speed with reference to the voltage applied at speed command input terminals X331 [X332] 56 and 14.

1.	Run a setup machine program so that the axis moves back and forth at 10% of maximum feedrate.  (Example:  BMC 4020 Max. feedrate (X, Y) = 19,990 and

(Z) = 15,000 mmpm, therefore 10% would be 1,999 and 1,500 mmpm respectively.

2.	Then adjust the potentiometer labeled “T”, tachometer, until the DAC output measured at terminals X331 [X332] 56 and 14 = +.95 +/- 0.005 and -95 +/- 0.005.

G.	At this point repeat steps in Sections VI and VII for any additional axis module in the system.  Once all axis modules have been setup and tested the system is ready to become operational.

VIII.	HURCO/SIEMENS PART IDENTIFICATION TABLE, SERVO

| System | Torque Nm | Hurco P/N (Motor) | Siemens Motor P/N | Rated Speed RPM | Siemens Drive P/N |
| --- | --- | --- | --- | --- | --- |
| BMC30 | 6.5 | 402-6011-018 | 1FT5066-1AF71-4FG0 C2 | 3000 | 6SN1123-1AA00-0AA0 (1-axis) 6SN1118-0AD11-0AA0 (1-axis) 6SN1123-1AB00-0AA0 (2-axis) 6SN1118-0AE11-0AA0 (2-axis) |
| BMC30HT | 10.0 | 402-6011-002 | 1FT5072-1AF71-1FG0 C2 | 3000 | 6SN1123-1AA00-0BA0 (1-axis) 6SN1118-0AD11-0AA0 (1-axis) 6SN1123-1AB00-0BA0 (2-axis) 6SN1118-0AE11-0AA0 (2-axis) |
| BMC4020HT | 10.0 | 402-6011-002 | 1FT5072-1AF71-1FG0 C2 | 3000 | 6SN1123-1AA00-0BA0 (1-axis) 6SN1118-0AD11-0AA0 (1-axis) 6SN1123-1AB00-0BA0 (2-axis) 6SN1118-0AE11-0AA0 (2-axis) |
| BMC4020SSM | 10.0 | 402-6011-002 | 1FT5072-1AF71-1FG0 C2 | 3000 | 6SN1123-1AA00-0BA0 (1-axis) 6SN1118-0AD11-0AA0 (1-axis) 6SN1123-0AB00-0BA0 (2-axis) 6SN1118-0AE11-0AA0 (2-axis) |

IX.	ULTIMAX 3 CONTROL PARAMETERS VERIFICATION, SPINDLE

Spindle Parameters are loaded by default (WITH SOFTWARE VERSION 1.62).  These parameters must be verified against the latest control parameters published to date 		 (757-4002-048).  DSP parameters may be edited in the “Tune Axis Parameter” screen.

Depress <ENTER>, 103, <ENTER> while in the “ATC and Machine Diagnostics” screen        of MANUAL machine mode.

X.	HURCO/SIEMENS PART IDENTIFICATION TABLE, SPINDLE

| System | Power (HP) | Hurco P/N (Motor) | Siemens Motor P/N | Motor RPM | Spindle RPM | X’mission Ratio | Siemens Drive P/N |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BMC30M | 15 HP | 402-6011-001 | 1PH6137-4NB49-Z Z=L69+K83+K03 E2 | 8000 | 8000 | 1.00 | 6SN1123-1AA00-0GA0 6SN1121-0BA13-0AA0 |
| BMC30HT | 15 HP | 402-6011-001 | 1PH6137-4NB49-Z Z=L69+K83+K03 E2 | 8000 | 8000 | 1.00 | 6SN1123-1AA00-0GA0 6SN1121-0BA13-0AA0 |
| BMC4020HT | 20 HP | 402-6011-015 | 1PH6163-4NB49-Z Z=L69+K83+K03 E2 | 6500 | 6500 | 1.00 | 6SN1123-1AA00-0FA0 6SN1121-0BA13-0AA0 |
| BMC4020SSM | 20 HP | 402-6011-015 | 1PH6163-4NB49-Z Z=L69+K83+K03 E2 | 6500 | 8125 | 1.25 | 6SN1123-1AA00-0FA0 6SN1121-0BA13-0AA0 |

XI.	SPINDLE START-UP SEQUENCE

A.	The following procedure requires that the I/R Infeed Module be operational as a prerequisite.  The I/R Infeed Module is the DC power source for the Spindle Module.

B.	Visually check to make sure that all I/O, encoder, ribbon, and power cables are securely terminated at the proper locations.  Also verify that the 600VDC bus bar links are securely connected.  They are located behind a plastic protective front cover.  CAUTION:  Once the drive system has been powered up high voltage is present.  It will take approximately 5 minutes to discharge when power is removed.

C.	Apply power to system via CB4 (32A), Spindle Module LED display should indicate “P-095” the first time the module unit is initiated.

XII.	IDENTIFY DRIVE AND MOTOR TYPE

A.	Enter “Drive Code” into Parameter “P-095”, identifies drive type to drive software.  This can be accomplished by pressing the “P” key on spindle keypad then the “+” or “-” key to increment or decrement the value as required.  Once the proper value from table below is entered simply press “P” to place the system back into parameter mode.

| System | Parameter P-095 “Drive Code” |
| --- | --- |
| D1 | BMC30M | 13(..0LA0), 8(..0GA0) |
| D1 | BMC30HT | 13(..0LA0), 8(..0GA0) |
|  | BMC4020HT | 10 |
|  | BMC4020SSM | 10 |

B.	Enter “Motor Code” into Parameter “P-096”, identifies motor type to drive software.  This can be accomplished by pressing the “P” key on spindle keypad then the “+” or “-” key to increment or decrement the value as required.  Once the proper value from table below is entered simply press “P” to place the system back into parameter mode.

| System | Parameter P-096 “Motor Code” |
| --- | --- |
| BMC30M | 133 |
| BMC30HT | 133 |
| BMC4020HT | 134 |
| BMC4020SSM | 134 |

C.	Verify “Encoder Pulse Code” value in Parameter “P-098”.  The motor measuring system should have encoder pulses per revolution equal to 2048.  If the value differs, change value from spindle keypad by using the “+” or “-” key to increment or decrement the value as required.

D.	Go to “Initialization” parameter “P-097”.  Change the parameter value by pressing the “+” key on the keypad.  The display should indicate “1”, then change to “P-000”.  The LCD’s should now indicate the “status” of the module with intermittently flashing “P-000”.  At this point specific functions and features can be implemented.

XIII.	PARAMETER LIST, MANUAL ENTRY

At this point proceed through the Parameter List in Attachment A (BMC30HT & BMC30M) or Attachment B (BMC4020HT & BMC4020SSM) and verify each parameter and change any parameter as necessary from the list.  Several parameters are predetermined from firmware and require no change.  These parameters can be identified with notation “mot 1” or “mot2” in description column.  It is important that all parameters agree with appropriate Parameter List for proper operation.

A.	In order to change machine specific parameters disable write protection by changing parameter “P-051” to “4H”.

B.	Toggle through each parameter in Attachment A or Attachment B and change the values to correspond to value settings in the list.

C.	After all parameter value settings have been incorporated and verified transfer the data into the drives EPROM by changing the value or parameter “P-052” to “1” to store the changes.  Once the data has been stored parameter “P-052” will return to “0”.

D.	Finally enable write protection parameter “P-051” to “0H” so that changes cannot be made inadvertently.

E.	Repeat this procedure whenever a change is necessary.

XIV.	SPINDLE ZERO RPM AND MAXIMUM RPM CALIBRATION

A.	To achieve the Spindle Zero Drift (spindle velocity of Zero RPM) proceed as follows:
Do not adjust the VR potentiometers on the MX4 board!  Leave them at their factory settings.  The range of adjustment available from the Siemens Spindle Module is sufficient to balance spindle offset.

1.	To ensure that the Spindle is in the Closed Loop Velocity mode, on the Ultimax Control select:  Auxiliary Mode; F4 (“System Config.”); F4 (“Display Machine Config.”); <ENTER>, 100, <ENTER>; F4 (“Spindle”); F1 (“Physical Parameter”).  Make change to Closed Loop Velocity if necessary.

2.	On the Ultimax Control select: MANUAL Mode; F2 (“Change Tool or Diagnostics”); F7 (“ATC and Machine Diagnostics”); <ENTER>, 101, <ENTER>; F6 (“Toggle Following Error Display”); F7 (“Axis Balance Adjust”); and F4 (“Spindle”).

3.	When the START CYCLE push-button is depressed, the Ultimax Control executes the following signal sequence - each stage lasting a few seconds, and its results (in counts) displayed on the Ultimax screen:

Zero signal: small (+) signal; small (-) signal.  Cycle repeats.

When the program starts, press the MOTION HOLD BUTTON, this will hold the DAC at zero output.  The spindle will probably rotate slowly, indicating a need for balance.

4.	Adjust parameter “P-015”, Offset Correction Speed Setpoint at the spindle drive.  Increase or decrease the hexadecimal value as necessary until the spindle stops rotating.  It will be necessary to use parameters “P-051” and “P-052” to invoke this change.  Verify the quality of the null by observing no change in the counts being displayed in the Following Error column and no physical spindle rotation.

B.	To calibrate The Maximum Spindle Speed parameter (ensuring that the Ultimax Control reflects true Spindle speed), proceed as follows:

1.	In MANUAL Mode, set the Manual Spindle Speed value to the maximum spindle speed of the machine.  Note this commanded (desired) value.

2.	The machine must now be put back into Open Loop mode.  On the Ultimax Control, select:  AUXILIARY Mode; F4 (“System Configuration”); F4 (“Display Machine Configuration”); <ENTER>, 100, <ENTER>; F4 (“Spindle”);  F1 (“Physical Parameters”); and F5 (“Open Loop”).

3.	Obtain a tachometer reading of Spindle RPM.  Note this measured value.

| Programmed RPM | Acceptable RPM Range | D2 |
| --- | --- | --- |
| 65 (4020HT) | 64-66* |  |
| 80 (SSM, 30’s) | 79-81* |  |
| 2000 (Both) | 1998-2002 |  |
| 4000 (4020HT) | 3996-4004 |  |
| 6000 (SSM, 30’s) | 5994-6006 |  |
| 6500 (4020HT) | 6493-6507 |  |
| 8000 (SSM, 30’s) | 7992-8008 |  |
| (*) Rounded to whole number |  |  |

4.	It is likely that there will be a discrepancy between the commanded or rated RPM and the measured Spindle speeds.  To offset this situation you may use the following formula to adjust the DAC voltage.  Calculate this new required voltage value (to two decimal places), and enter it into the Ultimax screen.  Use <ENTER>, 100, <ENTER> screen.

New “Max DAC” Voltage = (Desired RPM / Measured RPM) ( Old “Max DAC” Voltage

(Example:  Measured spindle speed = 5980 RPM with original DAC voltage on MAX3 screen of 9.5, but 6000 RPM is desired.  DAC voltage value should be changed to 6000/5980 ( 9.5 = 9.53V).

- The Spindle Drive RPM setup is complete.

XV.	ORIENT ZERO MARK SETUP WITH MOTOR ENCODER

A.	Procedure will work properly with motor encoder when spindle has a 1:1 ratio and a timing belt is used for transmission to ensure no motion loss.  To achieve an orient zero mark proceed as follows

1.	When using motor encoder, the spindle should be set for the shortest approach from either direction.  This is accomplished by setting parameter.
“P-149” to “21H”.

2.	Parameter “P-131” defines the number of encoder counts between two references signals taking into account the 1:1 ratio.  Set parameter to “2048”.  When the drive unit is powered up, the position counter is checked during the first one or two revolutions of the spindle.

3.	Parameter “P-141” set to “0H”, assigns motor encoder evaluation when required to orient spindle.

4.	Request transfer of switching parameters “P-141” for positioning by setting parameter “P-143” to “1”.  The parameter is automatically reset to “0”.

5.	Remove spindle drive key.

6.	Install ATC Setup Taper into the spindle and flange into the ATC.

7.	Move ATC to “right” position from the Ultimax Control/  Select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F1 (“Magazine Right”).

8.	Set the ATC height from Ultimax Control, select: MANUAL Mode; F2 (“Change Tool or Diagnostics”); F7 (“ATC and Machine Diagnostics”); <ENTER, 101, <ENTER>; Select the correct position, jog the Z-axis down until it is properly aligned with the tool changer.  Proper alignment is achieved when the Z-axis is positioned at a height relative to the tool changer which allows tools to be taken from and returned to the tool changer.  When the Z-axis is aligned, press softkey F1 (“Store Z Position”).

9.	Rotate the spindle at least one complete revolution by hand to a position so the drive key may be re-installed.

10.	Initialize the Internal Zero Mark by setting parameter “P-129” to “1H”, it will then automatically reset back to “0H”.  The new Zero Mark Offset is automatically stored in parameter “P-130”.

11.	Record the position actual value for zero mark offset from parameter “P-140”.

12.	Move ATC to “left” position from the Ultimax Control.  Select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F8 (“Magazine Left”).

B.	Verify orient zero mark setup.

1.	In MANUAL Mode, set the Manual Spindle Speed value to 3000 RPM.

2.	Depress <SPINDLE ON>, <START>.  Allow the spindle to reach desired speed.  Depress <SPINDLE OFF> to stop the spindle.

3.	On the Ultimax Control select:  MANUAL Mode; F6 (“Orient Spindle”).  Depress <CYCLE START>, spindle will orient itself the zero mark position.

4.	Observe parameter “P-140”, actual value zero mark offset.  The value should be (+) or (-) 1 count from the value recorded in step XV(A)11.  Also on the MANUAL display SPINDLE field will indicate ORIENTED.  If orient command is out of tolerance then repeat steps in section XV.

XVI.	ORIENT ZERO MARK SETUP WITH MOTOR ENCODER & PROXIMITY SENSOR

A.	Procedure will work properly with motor encoder and proximity switch when spindle has a 1:1.25 ratio and a timing belt is used for transmission to ensure no motion loss.  To achieve an orient zero mark proceed as follows:

1.E3	When using a proximity switch, the spindle is set for the shortest approach from either direction.  This is accomplished by setting parameter “P1-149” to “21H”.

2.	Parameter “P-131” defines the number of encoder counts between two reference signals taking into account the 1:1.25 ratio.  Set parameter to “1638”.  When the drive unit is powered up, the position counter is checked during the first one or two revolutions of the spindle.

3.	Parameter “P-141” set to “2H”, assigns proximity switch with motor encoder evaluation when required to orient spindle.

4.	Request transfer of switching parameters “P-141” for position by setting parameter “P-143” to “1”.  The parameter is automatically reset to “0”.

5.	Remove spindle drive key.

6.	Install ATC Setup Tool taper into the spindle and flange into the ATC.

- Move ATC to “right” position from the Ultimax Control.  Select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F1 (“Magazine Right”).

8.	Set the ATC height from Ultimax Control, select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F7 (“ATC and Machine Diagnostics”); <ENTER, 101, <ENTER>; Select the correct position, jog the Z-axis down until it is properly aligned with the tool changer.  Proper alignment is achieved when the Z-axis is positioned at a height relative to the tool changer which allows tools to be taken from and returned to the tool changer.  When the Z-axis is aligned, press softkey F1 (“Store Z Position”).

9.	Rotate the spindle at least one complete revolution by hand to a position so the drive key may be re-installed.

10.	Initialize the Internal Zero Mark by setting parameter “P-129” to “1H”, it will then automatically reset back to “0H”.  The new Zero Mark Offset is automatically stored in parameter “P-130”.

11.	Record the position actual value for zero mark offset from parameter “P-140”.

12.	Move ATC to “left” position from the Ultimax Control.  Select:  MANUAL Mode; F2 (“Change Tool or Diagnostics”); F8 (“Magazine Left”).

B.	Verify orient zero mark setup.

1.	In MANUAL Mode, set the Manual Spindle Speed value to 3000 RPM.

2.	Depress <SPINDLE ON>, <START>.  Allow the spindle to reach desired speed.  Depress <SPINDLE OFF> to stop the spindle.

3.	On the Ultimax Control select:  MANUAL Mode; F6 (“Orient Spindle”).  Depress <CYCLE START>, spindle will orient itself the zero mark position.

4.	Observe parameter “P-140”, actual value zero mark offset.  The value should

be (+) or (-) 1 count from the value recorded in step XVI(A)11.  Also on the MANUAL display SPINDLE field will indicate ORIENTED.  If orient command is out of tolerance then repeat steps in section XV.

XVII.	RE-INITIALIZE SPINDLE DRIVE

If for some reason it is necessary to re-initialize the spindle drive, reset all parameters to the original factory settings, perform the following steps:

A.	Set parameters:	“P-051” to “4H”
			“P-097” to “0H”
			“P-052” to “1H” it will automatically reset back to “0H”

B.	Power the system down, wait until the LCD’s extinguish.  Then power the system back up, the LCD readout will display parameter “P-095”.

C.	To restart and re-initialize the drive begin again at the beginning of these procedures for Siemens spindle drive.

| P No. | DESCRIPTION | DIMENSION | SETTING |
| --- | --- | --- | --- |
| P-000 | Operating display | - | N/A |
| P-001 | Speed setpoint | RPM | N/A |
| P-002 | Speed actual value | RPM | N/A |
| P-003 | Motor voltage | V | N/A |
| P-004 | Utilization | % | N/A |
| P-006 | DC link voltage | V | N/A |
| P-007 | Motor current | A | N/A |
| P-008 | Motor reactive power | kVA | N/A |
| P-009 | Motor active power | KW | N/A |
| P-010 | Motor temperature | (C | N/A |
| P-011 | Status of the binary inputs | hex | N/A |
| P-012 | Normalization, DAU nact display | % | 100.0 |
| P-013 | Normalization, DAU P/Pmax display | % | 100.0 |
| P-014 | Speed for max. motor useful speed mot 1 | RPM | 8000 |
| P-015 | Offset correction, speed setpoint | hex | (*) |
| P-016 | Ramp-up time, RFG | s | 0.01 |
| P-017 | Ramp-down time, RFG | s | 0.01 |
| P-018 | Smoothing time, speed setpoint smoothing | ms | 5 |
| P-019 | Degree of rounding-off, speed setpoint | dec | 0 |
| P-020 | Diagnostics, speed actual value | hex | N/A |
| P-021 | nmin for “nact ( nmin” signal mot 1 | RPM | 80 |
| P-022 | Shutdown speed, pulse cancellation mot 1 | RPM | 2 |
| P-023 | nx for “nact ( nx” signal mot 1 | RPM | 6000 |
| P-024 | Normalization, setpoint | V | 9.5 |
| P-026 | Normalization, DAU M/Mrated | % | 100.0 |
| P-027 | Toler, bandwidth for “nact = nset” signal mot 1 | RPM | 30 C3 |
| P-028 | Diagnostics | hex | N/A |
| P-029 | Speed limiting | RPM | 8000 |
| P-030 | Min. steady-state speed | RPM | 0 |
| P-031 | P gain, speed controller mot 1 | dec | 15.0 B1 |
| P-032 | Integral action time, speed controller mot 1 | ms | 20 |
| P-033 | Encoder resolution for NC | dec | 3 |
| P-035 | Smoothing time, torque setpoint mot 1 | ms | 3 |
| P-036 | Encoder phase error correction | dec | 0 |
| P-037 | Changeover speed, motor encoder evalu. mot 1 | RPM | 32000 |
| P-038 | Hysteresis, P-037 mot 1 | RPM | 50 |
| P-039 | 1st torque limit value mot 1 | % | 125 |
| P-040 | Regenerative limiting mot 1 | % | 100 |
| P-041 | 2nd torque limit value mot 1 | % | 50 |
| P-042 | Changeover speed for P-040 mot 1 | RPM | 500 |
| P-043 | Hysteresis, P-042 mot 1 | RPM | 20 |
| P-044 | Selection, torque setpoint smoothing | hex | 1H |
| P-045 | Switch-in speed, torque setpoint smooth mot 1 | RPM | 4000 |
| P-046 | Hysteresis, P-045 mot 1 | RPM | 50 |
| P-047 | Mdx for “Md ( Mdx” signal mot 1 | % | 90 |
| P-048 | Normalization, torque setpoint | % | 100 |
| P-049 | Offset, torque setpoint | hex | 0H |
| P-050 | Changeover speed from Md1 to Md2 mot 1 | RPM | 2100 |
| P-051 | Write protection | hex | N/A |
| P-052 | Transfer parameters into FEPROM | hex | N/A |
| P-053 | Control word | hex | 11H |
| P-054 | M19, speed setpoint normalization | RPM | 525 |
| P-055 | M19, speed setpoint offset correction | hex | 0H |
| P-056 | M19, changeover speed | RPM | 525 |
| P-058 | Switch-off threshold, rounding-off M19 | RPM | 0 |
| P-062 | M19 changeover threshold, I comp., speed cont. | RPM | 4 |
| P-063 | Max. motor temperature | (C | 150 |
| P-064 | Fixed temperature | (C | 0 |
| P-065 | Timer stage, motor temperature alarm | s | 240 |
| P-066 | Address, DAU 1 | hex | 3044H |
| P-067 | Shift factor, DAU 1 | dec | 0 |
| P-068 | Address, DAU 2 | hex | 3048H |
| P-069 | Shift factor, DAU 2 | dec | 0 |
| P-072 | Address, DAU 4 | hex | C04H |
| P-073 | Shift factor, DAU 4 | dec | 0 |
| P-074 | Offset, DAU 4 | hex | 0H |
| P-076 | Address, DAU 3 | hex | 3050H |
| P-077 | Shift factor, DAU 3 | dec | 0 |
| P-078 | Offset, DAU 1 | hex | 0H |
| P-079 | Offset, DAU 2 | hex | 0H |
| P-080 | Offset, DAU 3 | hex | 0H |
| P-081 | Terminal function assignment E1 | dec | 1 |
| P-082 | Terminal function assignment E2 | dec | 28 |
| P-083 | Terminal function assignment E3 | dec | 3 |
| P-084 | Terminal function assignment E4 | dec | 6 |
| P-085 | Terminal function assignment E5 | dec | 4 |
| P-086 | Terminal function assignment E6 | dec | 2 |
| P-087 | Terminal function assignment E7 | dec | 9 |
| P-088 | Terminal function assignment E8 | dec | 10 |
| P-089 | Terminal function assignment E9 | dec | 11 |
| P-090 | Control word | hex | 1H |
| P-091 | Frequency filter 1, HPC | Hz | 300 |
| P-092 | Quality filter 1, HPC | dec | 1.00 |
| P-093 | Offset correction, speed setpoint HPC | hex | 0H |
| P-094 | Normalization, speed setpoint HPC | RPM | 65 |
| P-095 | Power section code number | dec | 8 |
| P-096 | Motor code number mot 1 | dec | 133 |
| P-097 | Initialization | hex | 1H |
| P-098 | Encoder pulse number, motor measuring system | dec | 2048 |
| P-099 | Firmware release | dec | 2.30 |
| P-100 | Operating display | - | N/A |
| P-101 | Setpoint for open-loop torque controlled operation | % | N/A |
| P-102 | Speed actual value | RPM | N/A |
| P-103 | Frequency, torque setpoint filter mot 1 | Hz | 300 |
| P-104 | Quality, torque setpoint filter mot 1 | dec | 1.00 |
| P-106 | Smoothing time, speed setpoint, HPC | ms | 100 |
| P-107 | Frequency, filter 2 HPC | Hz | 300 |
| P-108 | Quality, filter 2 HPC | dec | 1.00 |
| P-109 | Torque limit, HPC | % | 100 |
| P-110 | Regenerative limit, HPC | % | 100 |
| P-111 | P-gain, speed controller HPC | dec | 10.0 |
| P-112 | Integral action time, speed controller HPC | ms | 20 |
| P-113 | Channel selection, speed setpoint | hex | 3H |
| P-114 | Normalization, speed setpoint, C axis | RPM | 65 |
| P-115 | Offset correction, speed setpoint, C axis | hex | 0H |
| P-116 | Correction, P-gain, current controller mot 1 | dec | 0 |
| P-117 | Selection, torque setpoint filter mot 1 | hex | 0H |
| P-118 | Type, torque setpoint filter mot 1 | hex | 0H |
| P-119 | Flux adaptation HPC | % | 100 |
| P-120 | Changeover speed, current contr. adapt. mot 1 | RPM | 2200 |
| P-121 | Position reference value 1 | dec | 0 |
| P-122 | Position reference value 2 | dec | 0 |
| P-123 | Position reference value, incremental | dec | 256 |
| P-124 | Position reference value 3 | dec | 0 |
| P-125 | Position reference value 4 | dec | 0 |
| P-126 | Bandwidth, integrator enable speed controller | dec | 10.0 |
| P-128 | Actual position reference value | dec | N/A |
| P-129 | Setting the internal zero mark | hex | 0H |
| P-130 | Zero mark offset | dec | (*) |
| P-131 | Max. pulse number between 2 zero marks | dec | 2048 |
| P-132 | Absol. pos. act. value without zero mark offset | dec | N/A |
| P-133 | Difference between 2 external zero marks | dec | N/A |
| P-134 | Initiation point for P-136 | degr. | 10.0 |
| P-135 | Initiation point for P-137 / P-138 | degr. | 2.0 |
| P-136 | P gain, gradient 1 | hex | 220H |
| P-137 | P gain, gradient 2 | hex | 220H |
| P-138 | P gain, gradient 2 (HMS) | hex | 44H |
| P-139 | Multiplier for braking parabola | hex | 100H |
| P-140 | Absol. pos. actual value with zero mark offset | dec | N/A |
| P-141 | Changeover parameter, positioning | hex | 0H |
| P-142 | Flag for speed increase | hex | 0H |
| P-143 | Transfer parameter P-141 | hex | 0H |
| P-144 | Response bandwidth, relay 1 | degr. | 2.00 C3 |
| P-145 | Response bandwidth, relay 2 | degr. | 5.00 |
| P-146 | Search speed for spindle positioning | RPM | -500 B1 |
| P-147 | Position counter status regarding the BERO | dec | N/A |
| P-148 | Motion window, spindle positioning | degr. | 1.0 |
| P-149 | Start-up parameter C axis/position | hex | 21H |
| P-150 | Board identification | hex | 300H |
| P-151 | Write protection | hex | N/A |
| P-152 | Transfer parameter into the EEPROM | hex | N/A |
| P-154 | Oscillation setpoint 1 | RPM | 0 |
| P-155 | Oscillation setpoint 2 | RPM | 0 |
| P-156 | Oscillation interval time 1 | ms | 1000 |
| P-157 | Oscillation interval time 2 | ms | 1000 |
| P-159 | Motor moment of inertia mot 1 | kgm2 | 0.085 |
| P-160 | Rated motor output mot 1 | kW | 7.9 |
| P-161 | Rated motor current mot 1 | A | 43.6 |
| P-162 | Rated motor voltage mot 1 | V | 159.0 |
| P-163 | Rated motor speed mot 1 | RPM | 525 |
| P-164 | Rated motor frequency mot 1 | Hz | 18.8 |
| P-165 | Motor no-load voltage mot 1 | V | 136.0 |
| P-166 | Motor no-load current mot 1 | A | 18.6 |
| P-167 | Stator resistance, cold mot 1 | m( | 139 |
| P-168 | Rotor resistance, cold mot 1 | m( | 101 |
| P-169 | Stator leakage reactance mot 1 | m( | 196 |
| P-170 | Rotor leakage reactance mot 1 | m( | 272 |
| P-171 | Main field reactance mot 1 | m( | 4150 |
| P-172 | Upper speed Xh characteristic mot 1 | RPM | 2200 |
| P-173 | Speed at the start of field weakening mot 1 | RPM | 1525 |
| P-174 | Max. motor speed mot 1 | RPM | 8000 |
| P-175 | Gain factor Xh characteristic mot 1 | % | 128 |
| P-176 | Stall torque reduction factor mot 1 | % | 100 |
| P-177 | Start calculation, motor 1 (P-096) | hex | N/A |
| P-179 | Select, min/max memory | hex | 0H |
| P-180 | Enable motor changeover (star/delta) | hex | 0H |
| P-181 | Address for min/max memory | hex | D02H |
| P-182 | Min. value min/max memory | hex | N/A |
| P-183 | Max. value min/max memory | hex | N/A |
| P-185 | Address for monitoring 1 | hex | C06H |
| P-186 | Threshold for monitoring 1 | hex | 0H |
| P-187 | Pull-in delay, monitoring 1 | s | 0.00 |
| P-188 | Drop-out delay, monitoring 1 | s | 0.00 |
| P-189 | Hysteresis, monitoring 1 | hex | 1H |
| P-190 | Address for monitoring 2 | hex | C06H |
| P-191 | Threshold for monitoring 2 | hex | 0H |
| P-192 | Pull-in delay, monitoring 2 | s | 0.00 |
| P-193 | Drop-out delay, monitoring 2 | s | 0.00 |
| P-194 | Hysteresis, monitoring 2 | hex | 1H |
| P-195 | Lower adaptation speed mot 1 | RPM | 1000 |
| P-196 | Upper adaptation speed mot 1 | RPM | 1200 |
| P-198 | P gain, upper adaptation speed mot 1 | dec | 24.0 |
| P-199 | Reduction factor, P gain mot 1 | % | 100 |
| P-201 | Integral action time, upper adapt. speed mot 1 | ms | 80 |
| P-202 | Reduction factor, integral action time mot 1 | % | 100 |
| P-203 | Control word, speed controller adapt. mot 1 | dec | 0 |
| P-206 | Selection, transient recorder | hex | N/A |
| P-207 | Set transient recorder | hex | N/A |
| P-208 | Address for start condition | hex | N/A |
| P-209 | Threshold for start condition | hex | N/A |
| P-210 | Address for stop condition | hex | N/A |
| P-211 | Threshold for the stop condition | hex | N/A |
| P-212 | Address, signal 1 | hex | N/A |
| P-213 | Address, signal 2 | hex | N/A |
| P-214 | Start trace output | hex | N/A |
| P-215 | Shift factor, signal 1 | dec | N/A |
| P-216 | Shift factor, signal 2 | dec | N/A |
| P-217 | Trigger signal 1 | hex | N/A |
| P-218 | Trigger signal 2 | hex | N/A |
| P-219 | Motor moment of inertia mot 2 | kgm2 | 0.085 |
| P-220 | Rated motor output mot 2 | kW | 7.9 |
| P-221 | Rated motor current mot 2 | A | 43.6 |
| P-222 | Rated motor voltage mot 2 | V | 159.0 |
| P-223 | Rated motor speed mot 2 | RPM | 525 |
| P-224 | Rated motor frequency mot 2 | Hz | 18.8 |
| P-225 | Motor no-load voltage mot 2 | V | 136.0 |
| P-226 | Motor no-load current mot 2 | A | 18.6 |
| P-227 | Stator resistance, cold mot 2 | m( | 139 |
| P-228 | Rotor resistance, cold mot 2 | m( | 101 |
| P-229 | Stator leakage reactance mot 2 | m( | 196 |
| P-230 | Rotor leakage reactance mot 2 | m( | 272 |
| P-231 | Main field reactance mot 2 | m( | 4150 |
| P-232 | Upper speed, Xh characteristic mot 2 | RPM | 2200 |
| P-233 | Speed at the start of field weakening mot 2 | RPM | 1525 |
| P-234 | Max. motor speed mot 2 | RPM | 8000 |
| P-235 | Gain factor Xh characteristic mot 2 | % | 128 |
| P-236 | Stall torque reduction factor mot 2 | % | 100 |
| P-237 | Start calculation, other motor | hex | N/A |
| P-238 | Motor code number mot 2 | dec | 133 |
| P-239 | Start calculation, motor 2 (P-238) | dec | N/A |
| P-241 | Programmable, signal 1 | dec | 2 |
| P-242 | Programmable, signal 2 | dec | 6 B1 |
| P-243 | Programmable, signal 3 | dec | 1 |
| P-244 | Programmable, signal 4 | dec | 4 |
| P-245 | Programmable, signal 5 | dec | 5 |
| P-246 | Programmable, signal 6 | dec | 9 |
| P-247 | Control word signal | hex | 0H |
| P-248 | Delay time, fault message F-11 | ms | 750 |
| P-249 | Memory loc. segment, monitor | hex | N/A |
| P-250 | Memory loc. address, monitor | hex | N/A |
| P-251 | Value display, monitor memory location | hex | N/A |
| P-254 | Display of active functions 1 | hex | N/A |
| P-255 | Display of active functions 2 | hex | N/A |
| P-258 | Speed for max. motor useful speed mot 2 | RPM | 8000 |
| P-260 | nmin for “nact ( nmin” signal mot 2 | RPM | 12 |
| P-261 | Shutdown speed, pulse cancellation mot 2 | RPM | 2 |
| P-262 | nx for “nact ( nx” signal | RPM | 6000 |
| P-263 | Toler. bandw. for “nact = nset” signal mot 2 | RPM | 20 |
| P-264 | Speed limiting mot 2 | RPM | 8000 |
| P-265 | P gain, speed controller mot 2 | dec | 32.0 |
| P-266 | Integral action time, speed controller mot 2 | ms | 20 |
| P-267 | Changeover speed, mot. encoder select. mot 2 | RPM | 32000 |
| P-268 | Hysteresis, P-267 mot 2 | RPM | 50 |
| P-269 | 1st torque limit mot 2 | % | 100 |
| P-270 | Regenerative limiting mot 2 | % | 100 |
| P-271 | 2nd torque limit mot 2 | % | 50 |
| P-272 | Changeover speed for P-270 mot 2 | RPM | 500 |
| P-273 | Hysteresis P-272 mot 2 | RPM | 20 |
| P-274 | Switch-in speed, torque setpoint smoothing mot 2 | RPM | 4000 |
| P-275 | Hysteresis P-274 mot 2 | RPM | 50 |
| P-276 | Frequency, torque setpoint filter mot 2 | Hz | 300 |
| P-277 | Quality, torque setpoint filter mot 2 | dec | 1.00 |
| P-278 | Correction, P-gain, current controller mot 2 | dec | 0 |
| P-280 | Select, torque setpoint filter mot 2 | hex | 0H |
| P-281 | Type of torque setpoint filer mot 2 | hex | 0H |
| P-283 | Lower adaptation speed mot 2 | RPM | 1000 |
| P-284 | Upper adaptation speed mot 2 | RPM | 1200 |
| P-285 | P-gain, upper adaptation speed mot 2 | dec | 24.0 |
| P-286 | Reduction factor, P-gain mot 2 | % | 100 |
| P-288 | Integral action time, upper adaptation speed mot 2 | ms | 80 |
| P-289 | Reduction factor, integral action time mot 2 | % | 100 |
| P-290 | Changeover speed from Md1 to Md2 mot 2 | RPM | 2100 |
| P-291 | Max. motor temperature (degrees Celsius) mot 2 | deg.C | 150 |
| P-292 | Changeover speed, current contr. adapt. mot 2 | RPM | 2200 |
| P-293 | Control word, speed controller adapt. mot 2 | dec | 0 |
| P-299 | Checksum parameters | hex | (*) |
| P-311 | Current for I/F open-loop control | % | 40.0 |
| P-312 | Frequency for I/F open-loop control | Hz | 0.0 |
| P-313 | Selection, I/F open-loop control | dec | 0H |
| P-316 | Display P-gain, current controller | dec | N/A |
| P-340 | Speed deviation, slip monitoring | % | 10.0 |
| P-341 | Torque reduction, slip monitoring | % | 50.0 |
| P-343 | Delay time, slip monitoring | ms | 200 |
| P-344 | Torque reduction speed, slip monitoring | %/ms | 0.50 |
| P-345 | Torque increase speed, slip monitoring | %/ms | 0.10 |
| P-346 | Hysteresis to P-340 | % | 0.00 |
| P-347 | Speed deviation, actual slip monitoring | % | N/A |

| P No. | DESCRIPTION | DIMENSION | SETTING |
| --- | --- | --- | --- |
| P-000 | Operating display | - | N/A |
| P-001 | Speed setpoint | RPM | N/A |
| P-002 | Speed actual value | RPM | N/A |
| P-003 | Motor voltage | V | N/A |
| P-004 | Utilization | % | N/A |
| P-006 | DC link voltage | V | N/A |
| P-007 | Motor current | A | N/A |
| P-008 | Motor reactive power | kVA | N/A |
| P-009 | Motor active power | KW | N/A |
| P-010 | Motor temperature | (C | N/A |
| P-011 | Status of the binary inputs | hex | N/A |
| P-012 | Normalization, DAU nact display | % | 100.0 |
| P-013 | Normalization, DAU P/Pmax display | % | 100.0 |
| P-014 | Speed for max. motor useful speed mot 1 | RPM | 6500 |
| P-015 | Offset correction, speed setpoint | hex | (*) |
| P-016 | Ramp-up time, RFG | s | 0.01 |
| P-017 | Ramp-down time, RFG | s | 0.01 |
| P-018 | Smoothing time, speed setpoint smoothing | ms | 5 |
| P-019 | Degree of rounding-off, speed setpoint | dec | 0 |
| P-020 | Diagnostics, speed actual value | hex | N/A |
| P-021 | nmin for “nact ( nmin” signal mot 1 | RPM | 65 |
| P-022 | Shutdown speed, pulse cancellation mot 1 | RPM | 2 |
| P-023 | nx for “nact ( nx” signal mot 1 | RPM | 6000 |
| P-024 | Normalization, setpoint | V | 9.5 |
| P-026 | Normalization, DAU M/Mrated | % | 100.0 |
| P-027 | Toler, bandwidth for “nact = nset” signal mot 1 | RPM | 30 C3 |
| P-028 | Diagnostics | hex | N/A |
| P-029 | Speed limiting | RPM | 6500 |
| P-030 | Min. steady-state speed | RPM | 0 |
| P-031 | P gain, speed controller mot 1 | dec | 15.0 B1 |
| P-032 | Integral action time, speed controller mot 1 | ms | 20 |
| P-033 | Encoder resolution for NC | dec | 3 |
| P-035 | Smoothing time, torque setpoint mot 1 | ms | 3 |
| P-036 | Encoder phase error correction | dec | 0 |
| P-037 | Changeover speed, motor encoder evalu. mot 1 | RPM | 32000 |
| P-038 | Hysteresis, P-037 mot 1 | RPM | 50 |
| P-039 | 1st torque limit value mot 1 | % | 125 |
| P-040 | Regenerative limiting mot 1 | % | 100 |
| P-041 | 2nd torque limit value mot 1 | % | 50 |
| P-042 | Changeover speed for P-040 mot 1 | RPM | 500 |
| P-043 | Hysteresis, P-042 mot 1 | RPM | 20 |
| P-044 | Selection, torque setpoint smoothing | hex | 1H |
| P-045 | Switch-in speed, torque setpoint smooth mot 1 | RPM | 4000 |
| P-046 | Hysteresis, P-045 mot 1 | RPM | 50 |
| P-047 | Mdx for “Md ( Mdx” signal mot 1 | % | 90 |
| P-048 | Normalization, torque setpoint | % | 100 |
| P-049 | Offset, torque setpoint | hex | OH |
| P-050 | Changeover speed from Md1 to Md2 mot 1 | RPM | 2000 |
| P-051 | Write protection | hex | N/A |
| P-052 | Transfer parameters into FEPROM | hex | N/A |
| P-053 | Control word | hex | 11H |
| P-054 | M19, speed setpoint normalization | RPM | 500 |
| P-055 | M19, speed setpoint offset correction | hex | 0H |
| P-056 | M19, changeover speed | RPM | 500 |
| P-058 | Switch-off threshold, rounding-off M19 | RPM | 0 |
| P-062 | M19 changeover threshold, I comp., speed cont. | RPM | 4 |
| P-063 | Max. motor temperature | (C | 150 |
| P-064 | Fixed temperature | (C | 0 |
| P-065 | Timer stage, motor temperature alarm | s | 240 |
| P-066 | Address, DAU 1 | hex | 3044H |
| P-067 | Shift factor, DAU 1 | dec | 0 |
| P-068 | Address, DAU 2 | hex | 3048H |
| P-069 | Shift factor, DAU 2 | dec | 0 |
| P-072 | Address, DAU 4 | hex | C04H |
| P-073 | Shift factor, DAU 4 | dec | 0 |
| P-074 | Offset, DAU 4 | hex | 0H |
| P-076 | Address, DAU 3 | hex | 3050H |
| P-077 | Shift factor, DAU 3 | dec | 0 |
| P-078 | Offset, DAU 1 | hex | 0H |
| P-079 | Offset, DAU 2 | hex | 0H |
| P-080 | Offset, DAU 3 | hex | 0H |
| P-081 | Terminal function assignment E1 | dec | 1 |
| P-082 | Terminal function assignment E2 | dec | 28 |
| P-083 | Terminal function assignment E3 | dec | 3 |
| P-084 | Terminal function assignment E4 | dec | 6 |
| P-085 | Terminal function assignment E5 | dec | 4 |
| P-086 | Terminal function assignment E6 | dec | 2 |
| P-087 | Terminal function assignment E7 | dec | 9 |
| P-088 | Terminal function assignment E8 | dec | 10 |
| P-089 | Terminal function assignment E9 | dec | 11 |
| P-090 | Control word | hex | 1H |
| P-091 | Frequency filter 1, HPC | Hz | 300 |
| P-092 | Quality filter 1, HPC | dec | 1.00 |
| P-093 | Offset correction, speed setpoint HPC | hex | OH |
| P-094 | Normalization, speed setpoint HPC | RPM | 65 |
| P-095 | Power section code number | dec | 10 |
| P-096 | Motor code number mot 1 | dec | 134 |
| P-097 | Initialization | hex | 1H |
| P-098 | Encoder pulse number, motor measuring system | dec | 2048 |
| P-099 | Firmware release | dec | 2.30 |
| P-100 | Operating display | - | N/A |
| P-101 | Setpoint for open-loop torque controlled operation | % | N/A |
| P-102 | Speed actual value | RPM | N/A |
| P-103 | Frequency, torque setpoint filter mot 1 | Hz | 300 |
| P-104 | Quality, torque setpoint filter mot 1 | dec | 1.00 |
| P-106 | Smoothing time, speed setpoint, HPC | ms | 100 |
| P-107 | Frequency, filter 2 HPC | Hz | 300 |
| P-108 | Quality, filter 2 HPC | dec | 1.00 |
| P-109 | Torque limit, HPC | % | 100 |
| P-110 | Regenerative limit, HPC | % | 100 |
| P-111 | P-gain, speed controller HPC | dec | 10.0 |
| P-112 | Integral action time, speed controller HPC | ms | 20 |
| P-113 | Channel selection, speed setpoint | hex | 3H |
| P-114 | Normalization, speed setpoint, C axis | RPM | 65 |
| P-115 | Offset correction, speed setpoint, C axis | hex | 0H |
| P-116 | Correction, P-gain, current controller mot 1 | dec | 0 |
| P-117 | Selection, torque setpoint filter mot 1 | hex | 0H |
| P-118 | Type, torque setpoint filter mot 1 | hex | 0H |
| P-119 | Flux adaptation HPC | % | 100 |
| P-120 | Changeover speed, current contr. adapt. mot 1 | RPM | 2300 |
| P-121 | Position reference value 1 | dec | 0 |
| P-122 | Position reference value 2 | dec | 0 |
| P-123 | Position reference value, incremental | dec | 256 |
| P-124 | Position reference value 3 | dec | 0 |
| P-125 | Position reference value 4 | dec | 0 |
| P-126 | Bandwidth, integrator enable speed controller | dec | 10.0 |
| P-128 | Actual position reference value | dec | N/A |
| P-129 | Setting the internal zero mark | hex | 0H |
| P-130 | Zero mark offset | dec | (*) |
| P-131 | Max. pulse number between 2 zero marks | dec | (**) |
| P-132 | Absol. pos. act. value without zero mark offset | dec | N/A |
| P-133 | Difference between 2 external zero marks | dec | N/A |
| P-134 | Initiation point for P-136 | degr. | 10.0 |
| P-135 | Initiation point for P-137 / P-138 | degr. | 2.0 |
| P-136 | P gain, gradient 1 | hex | 220H |
| P-137 | P gain, gradient 2 | hex | 220H |
| P-138 | P gain, gradient 2 (HMS) | hex | 44H |
| P-139 | Multiplier for braking parabola | hex | 100H |
| P-140 | Absol. pos. actual value with zero mark offset | dec | N/A |
| P-141 | Changeover parameter, positioning | hex | (**) |
| P-142 | Flag for speed increase | hex | 0H |
| P-143 | Transfer parameter P-141 | hex | 0H |
| P-144 | Response bandwidth, relay 1 | degr. | 2.00 C3 |
| P-145 | Response bandwidth, relay 2 | degr. | 5.00 |
| P-146 | Search speed for spindle positioning | RPM | -500 B1 |
| P-147 | Position counter status regarding the BERO | dec | N/A |
| P-148 | Motion window, spindle positioning | degr. | 1.0 |
| P-149 | Start-up parameter C axis/position | hex | 21H E4 |
| P-150 | Board identification | hex | 300H |
| P-151 | Write protection | hex | N/A |
| P-152 | Transfer parameter into the EEPROM | hex | N/A |
| P-154 | Oscillation setpoint 1 | RPM | 0 |
| P-155 | Oscillation setpoint 2 | RPM | 0 |
| P-156 | Oscillation interval time 1 | ms | 1000 |
| P-157 | Oscillation interval time 2 | ms | 1000 |
| P-159 | Motor moment of inertia mot 1 | kgm2 | 0.170 |
| P-160 | Rated motor output mot 1 | kW | 11.5 |
| P-161 | Rated motor current mot 1 | A | 66.2 |
| P-162 | Rated motor voltage mot 1 | V | 149.0 |
| P-163 | Rated motor speed mot 1 | RPM | 500 |
| P-164 | Rated motor frequency mot 1 | Hz | 17.7 |
| P-165 | Motor no-load voltage mot 1 | V | 128.0 |
| P-166 | Motor no-load current mot 1 | A | 27.8 |
| P-167 | Stator resistance, cold mot 1 | m( | 87 |
| P-168 | Rotor resistance, cold mot 1 | m( | 48 |
| P-169 | Stator leakage reactance mot 1 | m( | 131 |
| P-170 | Rotor leakage reactance mot 1 | m( | 145 |
| P-171 | Main field reactance mot 1 | m( | 2620 |
| P-172 | Upper speed Xh characteristic mot 1 | RPM | 2300 |
| P-173 | Speed at the start of field weakening mot 1 | RPM | 1600 |
| P-174 | Max. motor speed mot 1 | RPM | 6500 |
| P-175 | Gain factor Xh characteristic mot 1 | % | 141 |
| P-176 | Stall torque reduction factor mot 1 | % | 100 |
| P-177 | Start calculation, motor 1 (P-096) | hex | N/A |
| P-179 | Select, min/max memory | hex | 0H |
| P-180 | Enable motor changeover (star/delta) | hex | 0H |
| P-181 | Address for min/max memory | hex | D02H |
| P-182 | Min. value min/max memory | hex | N/A |
| P-183 | Max. value min/max memory | hex | N/A |
| P-185 | Address for monitoring 1 | hex | C06H |
| P-186 | Threshold for monitoring 1 | hex | 0H |
| P-187 | Pull-in delay, monitoring 1 | s | 0.00 |
| P-188 | Drop-out delay, monitoring 1 | s | 0.00 |
| P-189 | Hysteresis, monitoring 1 | hex | 1H |
| P-190 | Address for monitoring 2 | hex | C06H |
| P-191 | Threshold for monitoring 2 | hex | 0H |
| P-192 | Pull-in delay, monitoring 2 | s | 0.00 |
| P-193 | Drop-out delay, monitoring 2 | s | 0.00 |
| P-194 | Hysteresis, monitoring 2 | hex | 1H |
| P-195 | Lower adaptation speed mot 1 | RPM | 1000 |
| P-196 | Upper adaptation speed mot 1 | RPM | 1200 |
| P-198 | P gain, upper adaptation speed mot 1 | dec | 24.0 |
| P-199 | Reduction factor, P gain mot 1 | % | 100 |
| P-201 | Integral action time, upper adapt. speed mot 1 | ms | 80 |
| P-202 | Reduction factor, integral action time mot 1 | % | 100 |
| P-203 | Control word, speed controller adapt. mot 1 | dec | 0 |
| P-206 | Selection, transient recorder | hex | N/A |
| P-207 | Set transient recorder | hex | N/A |
| P-208 | Address for start condition | hex | N/A |
| P-209 | Threshold for start condition | hex | N/A |
| P-210 | Address for stop condition | hex | N/A |
| P-211 | Threshold for the stop condition | hex | N/A |
| P-212 | Address, signal 1 | hex | N/A |
| P-213 | Address, signal 2 | hex | N/A |
| P-214 | Start trace output | hex | N/A |
| P-215 | Shift factor, signal 1 | dec | N/A |
| P-216 | Shift factor, signal 2 | dec | N/A |
| P-217 | Trigger signal 1 | hex | N/A |
| P-218 | Trigger signal 2 | hex | N/A |
| P-219 | Motor moment of inertia mot 2 | kgm2 | 0.170 |
| P-220 | Rated motor output mot 2 | kW | 11.5 |
| P-221 | Rated motor current mot 2 | A | 66.2 |
| P-222 | Rated motor voltage mot 2 | V | 149.0 |
| P-223 | Rated motor speed mot 2 | RPM | 500 |
| P-224 | Rated motor frequency mot 2 | Hz | 17.7 |
| P-225 | Motor no-load voltage mot 2 | V | 128.0 |
| P-226 | Motor no-load current mot 2 | A | 27.8 |
| P-227 | Stator resistance, cold mot 2 | m( | 87 |
| P-228 | Rotor resistance, cold mot 2 | m( | 48 |
| P-229 | Stator leakage reactance mot 2 | m( | 131 |
| P-230 | Rotor leakage reactance mot 2 | m( | 145 |
| P-231 | Main field reactance mot 2 | m( | 2620 |
| P-232 | Upper speed, Xh characteristic mot 2 | RPM | 2300 |
| P-233 | Speed at the start of field weakening mot 2 | RPM | 1600 |
| P-234 | Max. motor speed mot 2 | RPM | 6500 |
| P-235 | Gain factor Xh characteristic mot 2 | % | 141 |
| P-236 | Stall torque reduction factor mot 2 | % | 100 |
| P-237 | Start calculation, other motor | hex | N/A |
| P-238 | Motor code number mot 2 | dec | 134 |
| P-239 | Start calculation, motor 2 (P-238) | dec | N/A |
| P-241 | Programmable, signal 1 | dec | 2 |
| P-242 | Programmable, signal 2 | dec | 6 B1 |
| P-243 | Programmable, signal 3 | dec | 1 |
| P-244 | Programmable, signal 4 | dec | 4 |
| P-245 | Programmable, signal 5 | dec | 5 |
| P-246 | Programmable, signal 6 | dec | 9 |
| P-247 | Control word signal | hex | 0H |
| P-248 | Delay time, fault message F-11 | ms | 750 |
| P-249 | Memory loc. segment, monitor | hex | N/A |
| P-250 | Memory loc. address, monitor | hex | N/A |
| P-251 | Value display, monitor memory location | hex | N/A |
| P-254 | Display of active functions 1 | hex | N/A |
| P-255 | Display of active functions 2 | hex | N/A |
| P-258 | Speed for max. motor useful speed mot 2 | RPM | 6500 |
| P-260 | nmin for “nact ( nmin” signal mot 2 | RPM | 12 |
| P-261 | Shutdown speed, pulse cancellation mot 2 | RPM | 2 |
| P-262 | nx for “nact ( nx” signal | RPM | 6000 |
| P-263 | Toler. bandw. for “nact = nset” signal mot 2 | RPM | 20 |
| P-264 | Speed limiting mot 2 | RPM | 6500 |
| P-265 | P gain, speed controller mot 2 | dec | 32.0 |
| P-266 | Integral action time, speed controller mot 2 | ms | 20 |
| P-267 | Changeover speed, mot. encoder select. mot 2 | RPM | 32000 |
| P-268 | Hysteresis, P-267 mot 2 | RPM | 50 |
| P-269 | 1st torque limit mot 2 | % | 100 |
| P-270 | Regenerative limiting mot 2 | % | 100 |
| P-271 | 2nd torque limit mot 2 | % | 50 |
| P-272 | Changeover speed for P-270 mot 2 | RPM | 500 |
| P-273 | Hysteresis P-272 mot 2 | RPM | 20 |
| P-274 | Switch-in speed, torque setpoint smoothing mot 2 | RPM | 4000 |
| P-275 | Hysteresis P-274 mot 2 | RPM | 50 |
| P-276 | Frequency, torque setpoint filter mot 2 | Hz | 300 |
| P-277 | Quality, torque setpoint filter mot 2 | dec | 1.00 |
| P-278 | Correction, P-gain, current controller mot 2 | dec | 0 |
| P-280 | Select, torque setpoint filter mot 2 | hex | 0H |
| P-281 | Type of torque setpoint filer mot 2 | hex | 0H |
| P-283 | Lower adaptation speed mot 2 | RPM | 1000 |
| P-284 | Upper adaptation speed mot 2 | RPM | 1200 |
| P-285 | P-gain, upper adaptation speed mot 2 | dec | 24.0 |
| P-286 | Reduction factor, P-gain mot 2 | % | 100 |
| P-288 | Integral action time, upper adaptation speed mot 2 | ms | 80 |
| P-289 | Reduction factor, integral action time mot 2 | % | 100 |
| P-290 | Changeover speed from Md1 to Md2 mot 2 | RPM | 2000 |
| P-291 | Max. motor temperature (degrees Celsius) mot 2 | deg.C | 150 |
| P-292 | Changeover speed, current contr. adapt. mot 2 | RPM | 2300 |
| P-293 | Control word, speed controller adapt. mot 2 | dec | 0 |
| P-299 | Checksum parameters | hex | (*) |
| P-311 | Current for I/F open-loop control | % | 40.0 |
| P-312 | Frequency for I/F open-loop control | Hz | 0.0 |
| P-313 | Selection, I/F open-loop control | dec | 0H |
| P-316 | Display P-gain, current controller | dec | N/A |
| P-340 | Speed deviation, slip monitoring | % | 10.0 |
| P-341 | Torque reduction, slip monitoring | % | 50.0 |
| P-343 | Delay time, slip monitoring | ms | 200 |
| P-344 | Torque reduction speed, slip monitoring | %/ms | 0.50 |
| P-345 | Torque increase speed, slip monitoring | %/ms | 0.50 |
| P-346 | Hysteresis to P-340 | % | 0.00 |
| P-347 | Speed deviation, actual slip monitoring | % | N/A |

#### ORIENT SPECIFIC FUNCTIONS FOR “HT” VS. “SSM”

| P No. | BMC4020HT | BMC4020SSM |
| --- | --- | --- |
| P-131 | 2048 | 1638 |
| P-141 | 0H | 2H |

# Text boxes

LED Status Indicator

R1

R3

R2

R4

Y1

G1