K-150 instruction for programming the 7878

And its Integrated Imager Module

7878 must contain firmware version 497-0472618 or later!

Please refer to scanner website if you need to reflash the 7878:

http://www5.ncr.com/support/support_drivers_patches.asp?Class=retail_RealScan

K150-full-instructions-with-2D.doc

Programming the 7878

Program the 7878 to:

1.  Beep whenever it receives valid barcode data from the new imager module through the USB host port (the scanner does not beep by default for barcodes received by the imager);

2.  Allow the pass-through of 2D data to the POS without the 7878 scanner itself having the capability to read that type of barcode;

3.  Enable K150 mode.

PROGRAM MODE

HEX 4

HEX 0

HEX 5   (beep at HH input)

HEX 7

HEX F

HEX 9   (pass 2D thru)

HEX 8

HEX B

HEX 1   (enable K150)

SAVE&RESET	(Enable 2D pass-thru function of all 2D types)*

* The passed-through PDF data is transmitted in ASCII format when RS232 Serial or NCR USB is in use.  This is the data format required by NCR OPOS for 2D barcodes.

Programming the integrated imager

Your imager has only a limited number of symbologies enabled from the factory.

Defaults:

UPC-A

UPC-E

EAN-8

EAN-13

PDF417

GS1 Databar 14 (RSS-14)

GS1 Databar Expanded (RSS-14 Expanded)

GS1 Databar Coupons

Any symbology other than what is explicitly listed above must be enabled with barcodes.

You can either enable ALL the barcodes the imager reads, or selectively turn one on at a time, in case you don’t accidently want to scan something not expected.

See PAGE 9 of this document for the barcodes that default the imager back to what is shown above.

Please check the chart below for every extra symbology you enable to see if additional programming needs done ON THE 7878 to make the scanner read it.

| Symbology Type | Included in the "Enable All" barcode? | Action required on 7874 to make this read? |
| --- | --- | --- |
| EAN/JAN-8 | yes | enabled by Default |
| EAN/JAN-13 | yes | enabled by Default |
| UPC-A | yes | enabled by Default |
| UPC-E | yes | enabled by Default |
| UPC-A+2 | yes | Need PM 13E120 S&R |
| UPC-A+5 | yes | Need PM 13E120 S&R |
| UPC-E+2 | yes | Need PM 13E120 S&R |
| UPC-E+5 | yes | Need PM 13E120 S&R |
| EAN/JAN-8+2 | yes | Need PM 13E120 S&R |
| EAN/JAN-8+5 | yes | Need PM 13E120 S&R |
| EAN/JAN-13+2 | yes | Need PM 13E120 S&R |
| EAN/JAN-13+5 | yes | Need PM 13E120 S&R |
| INTERLEAVED 2 of 5 | yes | Need PM 15A1 S&R |
| CODE 39 | yes | Need PM 14A1 S&R |
| CODE 128 | yes | Need PM 17A1 S&R |
| CODABAR | yes | Need PM 1AA1 S&R |
| CODE 93 | yes | ** |
| UPC/EAN-128 | yes | Need PM17A1, 17C1 S&R |
| GS1-DATABAR (RSS) including LIMITED | yes | GS1-14 (RSS-14) : enabled by Default GS1-Limited: N/A |
| DATABAR EXPANDED | yes | enabled by Default |
| PDF417 | yes | ** |
| MAXICODE | yes | ** |
| DATA MATRIX | yes | ** |
| QR CODE | yes | ** |
| Micro QR Code | yes | ** |
| AZTEC | yes | ** |

** Requires K150 and the 7878 programming shown on page 2 of this document.

Use this barcode to enable ALL THE IMAGER’S supported barcode types:

Check the chart above if you do this!

Individual Symbology Enable barcodes

Please scan the following barcodes in the vertical window of the 7878, so the integrated imager can see them and read them.  You might need to fold this paper and the next so only one barcode shows at a time.

You do NOT need to scan all of these.  Only scan the ones you need to use in the field.

Note there will likely be no audible feedback (beep) when the imager reads them, so hold the programming barcode there for a couple seconds.

Currently, the only way to know if the programming tag “took” or not is to try scanning the sample 2D barcode (located on last page of these instructions) of the type you enabled.

-----------------------------------fold------------------------------------------

(enables MicroQR too)

-----------------------------------fold------------------------------------------

-----------------------------------fold------------------------------------------

-----------------------------------fold------------------------------------------

Scanning these two barcodes takes the imager back to the defaults

shown on page 3.

rtllts1	Enable retail lights control

rtlsen1	Lights enabled by default

tstmnu1	Test menu enabled

allena0	Disable All Codes

upaena1	UPCA enabled

upeen01	UPC E enabled

e13ena1	EAN-13 / JAN-13 enabled

ea8ena1	EAN-8 / JAN-8 enabled

rssean1	GS1 Databar-14 (RSS) enabled

rseena1	GS1 Databar-Expanded (RSS-E) enabled

pdfena1	PDF417 enabled

papspc	Enable streaming presentation mode for mobile phones

papsph	IBM Surepos 4B communication mode

decaux0	Prevent decoding of stored images received after a disable command.  (10/13)

Sample 2D Barcodes

Sample PDF417:

Sample QR Code

Sample Maxi Code:

# Text boxes

IMPORTANT

The following 7878 programming instructions are ONLY meant to enable the newly installed imager module.

They are NOT intended to be a substitute for the customer’s already-programmed parameters.

Do NOT scan the NCR 7878 DEFAULT barcode at any time when installing the Imager Module or the Customer’s original parameters will be lost and their scanners will stop working.

WARNING!

Enabling certain symbologies on the imager when they are not separately enabled on the 7878 causes an error tone when the imager scans it.  They must be enabled on both scanners.

Please pay attention to the third column in the chart below.

IMPORTANT:  BEWARE OF THIS

If the imager has 128 enabled, it is possible it will see, read, and then transmit the NCR programming tag to the 7878’s USB port as data.  When this happens, the 7878 will give a ‘Bad Tone’ when you scan a programming barcode.  If this happens, start over with the RESET barcode, then use ONLY the horizontal window to scan 7878 programming tags.