Δ ANTAR   ITALIA  s.r.l.

Last generation – the van of technology

## GLASS  SHINING

MINI

#### PER  ASCIUGARE  E  LUCIDARE  I  BICCHIERI

##### TO  DRY  AND  POLISH  GLASSES

POUR  SECHER  ET  BRILLIANTER  LES  VERRES

### GENERALITIES

After washing, the glasses need a manual work to keep away the halos and the water traces.

This operation is not gratifying and risks breaking same glasses due to the twist of the stem glasses.

The Glass Shining makes this work easier allowing you to dry and shin the glasses coming out of the washing machine.

It is a compact machine endowed of eight rolling brushes covered with soft fringes 100% natural fibre, which allows dealing with two glasses at the same time.

The glasses are put upset around the two central brushes and are perfectly dried and shined in and out.

The brushes are made in three different sizes: two small, four medium, 2 large and can be easily changed one another according to the size and shape of your glasses.

The shafts on which are fixed the brushes have three stop positions thanks to a movable screw. You can move up or dawn each brush to adjust them better to the kind of the glasses.

The brushes absorb the humidity remained on the glasses but are kept dried by two jets of hot air coming from the two lateral chimneys. If dark, they can be washed in tepid water.

The hot air is inhaled from the bottom of the machine protected by a filter and sterilized by a germicide u.v.c. lamp to assure the maximum of hygiene according to the actual H.A.C.C.P. rules.

GLASS SHINING – basic running data

An engine grants the rotation of the brushes using a system of pulleys and driving belts.

One fan pushes the air thought the resistances , ruled by a thermostat,  into the lateral drying chimney.

A protected opening allows to verify if the germicide lamp is working.

A waterproof switch starts and stops the machine.

A waterproof switch ( I – O –II ) allows you to choose the heating power according with your work method.

Two fuses protect the engine and the resistance and you can easily reach them from outside.

Technical data:

Engine						           60  watt

resistance with thermostat			  0 -   600  watt

tangential fan					           30  watt

Total installed power	                                   100 - 700  watt

Electric connection :			                    Shuko

Feeding:					        220  volt mono phase

Fuses:				    		        2 A – delayed + 6,50 A - delayed

Sizes:						        width	      cm. 26

length	      cm. 37

height	      cm. 52

Weight:				                    kg.  12

Productivity:				                    up to 250 glasses / hour

Installation:

After taking away the Glass Shining from the packing, place it on a working plate if possible near the washing machine for glasses.

Connect it to an electric 220/240 volt plug.

Be sure that the machine is perfectly flat and the air intake is non obstructed.

Rule the height of the brushes according to the shape of the glasses.

If you have glasses with flat bottom, we suggest to line the central brushes with the lateral ones.

If you use stem glasses, we suggest to place the central brushe lower than the later ones to allow you to dry the stems.

A waterproof switch – on / of – let you start and stop the machine.

A waterproof switch  I – O – II allows you to choose the heating power you prefer.

Pos. O = no heating

Pos. I  = medium heating

Pos. II = maximum heating

Working:

Put the brushes according to the shape and size of your glasses:

Small size:		small goblets, flûtes etc.

Medium size:		glasses for water, medium goblets, and glasses for whisky etc.

Large size:		ballons, tankards  etc.

Take a glass from the basket of the washing machine, still whet and hot, and place it around the central brush.

After few seconds, it will be perfectly dry and shining. Use cotton glovers to absorb the remaining humidity on the bottom of the glasses.

If the glasses are to dry and the water stains are “ glued “ to the crystal make it wet by hot water or steam.

Be sure that the germicide lamp is working looking , from the apposite opening, the characteristic blue light .

Let the machine work also when you don’t use it to let the brushes to dry completely. Let the machine on for a few minutes to complete the drying even at the end of the work.

Maintenance:

Glass Shining doesn’t need any maintenance but only a careful cleaning.

The filter on the air opening – placed on the bottom of the machine – must be cleaned at least once a week.

Be sure that the working plane , on which the machine is placed, is clean to avoid to inspire powder and dirt.

The brushes must be always clean. When necessary, wash them in tepid water and dry them on the working machine.

For any technical problems, ask for the technical department.

Pay attention:

Use only original spare parts. If you temper with the machine or don’t use the original spare parts, your guarantee will be operating no more.

The Glass Shining is homologated CE and it is in conformity with the actual Haccp European law.

Each machine is accompanied with the manual and the conformity declaration.

The characteristic data and the code number are on the plate placed sidewise.

Glass Shining Mini is product by

Antar Italia s.r.l.

via Ressi 11 – 20125 Milan  - Italy

Tel. +39-02-66710938

# Fax +39-02-66710100

e mail :  antarit@iol.it

www.antiritalia.it

Technical department: 333-53.07.021 - 348-372.33.96

Δ ANTAR   ITALIA  s.r.l.

via Ressi 11 – 20125 Milano – tel. 02-66710938 – fax 02-66710100 – cell. 335.6026667

e mail: antarit@iol.it -  web : www.antaritalia.it

# CONFORMITY  DECLARATION

We declare, hereby, that the under mentioned machine respects all the demands of “ CEE Directives “ n° 89/392  - 89/336 – 73/23 and the following modifications and of EN60 204/1 – 17025 – 45001.

# Producer:					Antar Italia srl.

via Ressi 11

20125 Milano - Italy

Model:					Glass Shining Mini

Feeding:					220/240 volt - 50 Htz

Engine:					  60  w

# Heating:	        			     0 -  600  w

Total power:		        		  100 - 700 w

Milan, june 2005						Antar Italia srl.

## Cap. sociale i.v. € 25.000 – Reg. Imp. di  Mi: c.f. e p.iva 03302620962 - Rea: 1665713