# OMTD

# OPOS FOR MAGTEK DEVICES

# PROGRAMMING REFERENCE MANUAL

# Manual Part Number:  99875144 Rev 3P

MAY 2003

PRELIMINARY

REGISTERED TO ISO 9001:2000

# 20725 South Annalee  Avenue

Carson, CA 90746

Phone:  (310) 631-8602

FAX:  (310) 631-3956

Technical Support: (888) 624-8350

www.magtek.com

Copyright© 1999-2003

MagTek®, Inc.

Printed in the United States of America

Information in this document is subject to change without notice.  No part of this document may be reproduced or transmitted in any form or by any means, electronic or mechanical, for any purpose, without the express written permission of MagTek, Inc.

# MagTek is a registered trademark of MagTek, Inc.

# REVISIONS

| Rev Number | Date | Notes |
| --- | --- | --- |
| 1 | 5 Oct 99 | Initial Release |
| 2 | 17 Feb 00 | Section 2: Added "Registering an OLE Programmatic ID Alias for OPOS Control Object." Added Figure 2-1; Section 3: Added "Registering an OLE Programmatic ID Alias for OPOS Control Object." |
| 3 | XX Feb 03 | Engineering Update for MTD Software Release 1.12. Front Matter: Added ISO line to logo and Software License and removed Limited Warranty. |

SOFTWARE LICENSE AGREEMENT

IMPORTANT: YOU SHOULD CAREFULLY READ ALL THE TERMS, CONDITIONS AND RESTRICTIONS OF THIS LICENSE AGREEMENT BEFORE INSTALLING THE SOFTWARE PACKAGE. YOUR INSTALLATION OF THE SOFTWARE PACKAGE PRESUMES YOUR ACCEPTANCE OF THE TERMS, CONDITIONS, AND RESTRICTIONS CONTAINED IN THIS AGREEMENT. IF YOU DO NOT AGREE WITH THESE TERMS, CONDITIONS, AND RESTRICTIONS, PROMPTLY RETURN THE SOFTWARE PACKAGE AND ASSOCIATED DOCUMENTATION TO ABOVE ADDRESS ATTENTION: CUSTOMER SUPPORT.

TERMS, CONDITIONS AND RESTRICTIONS

MagTek, Incorporated (the "Licensor") owns and has the right to distribute the described software and documentation, collectively referred to as the "Software".

LICENSE: Licensor grants you (the "Licensee") the right to use the Software in conjunction with MagTek products.

LICENSEE MAY NOT COPY, MODIFY OR TRANSFER THE SOFTWARE IN WHOLE OR IN PART EXCEPT AS EXPRESSLY PROVIDED IN THIS AGREEMENT. Licensee may not decompile, disassemble or in any other manner attempt to reverse engineer the Software. Licensee shall not tamper with, bypass or alter any security features of the software or attempt to do so.

TRANSFER: Licensee may not transfer the Software or license to the Software to another party without prior written authorization of the Licensor. If Licensee transfers the Software without authorization, all rights granted under this Agreement are automatically terminated.

COPYRIGHT: The Software is copyrighted. Licensee may not copy the Software except for archival purposes or to load for execution purposes. All other copies of the Software are in violation of this Agreement.

TERM: This Agreement is in effect as long as Licensee continues the use of the Software. The Licensor also reserves the right to terminate this Agreement if Licensee fails to comply with any of the terms, conditions or restrictions contained herein. Should Licensor terminate this Agreement due to Licensee's failure to comply, Licensee agrees to return the Software to Licensor. Receipt of returned Software by the Licensor shall mark the termination.

LIMITED WARRANTY: Licensor warrants to the Licensee that the disk(s) or other media on which the Software is recorded to be free from defects in material or workmanship under normal use. THE SOFTWARE IS PROVIDED AS IS WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESS OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE. Because of the diversity of conditions and PC hardware under which the Software may be used, Licensor does not warrant that the Software will meet Licensee specifications or that the operation of the Software will be uninterrupted or free of errors.

IN NO EVENT WILL LICENSOR BE LIABLE FOR ANY DAMAGES, INCLUDING ANY LOST PROFITS, LOST SAVINGS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES ARISING OUT OF THE USE OR INABILITY TO USE THE SOFTWARE. Licensee's sole remedy in the event of a defect in material or workmanship is expressly limited to replacement of the Software disk(s) if applicable.

GOVERNING LAW: If any provision of this Agreement is found to be unlawful, void or unenforceable, that provision shall be removed from consideration under this Agreement and will not affect the enforceability of any of the remaining provisions. This Agreement shall be governed by the laws of the State of California and shall insure to the benefit of MagTek, Incorporated, its successors or assigns.

ACKNOWLEDGMENT: LICENSEE ACKNOWLEDGES THAT HE HAS READ THIS AGREEMENT, UNDERSTANDS ALL OF ITS TERMS, CONDITIONS AND RESTRICTIONS AND AGREES TO BE BOUND BY THEM. LICENSEE ALSO AGREES THAT THIS AGREEMENT SUPERSEDES ANY AND ALL, VERBAL AND WRITTEN, COMMUNICATIONS BETWEEN LICENSOR AND LICENSEE OR THEIR ASSIGNS RELATING TO THE SUBJECT MATTER OF THIS AGREEMENT.

QUESTIONS REGARDING THIS AGREEMENT SHOULD BE ADDRESSED IN WRITING TO MAGTEK, INCORPORATED, ATTENTION: CUSTOMER SUPPORT, AT THE ABOVE ADDRESS OR E-MAILED TO support@magtek.com

# TABLE OF CONTENTS

Section 1.  Features and Requirements	1

Features	1

Requirements	1

Interfacing to Applications	2

Interfacing to the Device	2

Supported Device Classes	2

Operation	3

Compatibility	3

Configuration	4

Reference Documents	4

Section 2.  Installation	5

OMTD Installation Notes	5

Registering OLE Programmatic ID Alias for OPOS Control Object	6

Modifying and Removing Devices	6

Section 3.  Implementation notes	9

Single Service Object	9

Potential Problems in Windows 95/98	9

Modifying OMTD Device Configuration	9

Opening the device	10

Registering OLE Programmatic ID Alias for OPOS Control Object	10

Device Power Reporting	11

Saving Device Settings Across Claim/Release	11

Error Processing	11

Reporting	11

Incompatibility Issues	12

Section 4.  Control Objects	13

Common Interfaces	13

OLE Interfaces	13

Event Methods	13

Common Properties	14

Magnetic Stripe Reader (MSR) Device Class	17

MSR Properties	17

MSR Methods	18

MICR Device Class	18

MICR Properties	18

MICR Methods	19

PINPad Device Class	19

PINPad Properties	20

PINPad Methods	21

Line Display Device Class	21

LDSP Properties	22

LDSP Methods	23

Use Cases	24

Using an OMTD Control	24

Supported Device Features	25

Common Features	25

MSR Device Class	26

MICR Device Class	26

PINPad Device Class	27

Line Display Device Class	28

Appendix A.  Glossary	31

Index	33

# FIGURE

OMTD Program Controlled Devices	vi

# OMTD Program Controlled Devices

# Section 1.  Features and Requirements

The OMTD program is an extension of the MagTek Device Driver Program (MTD).  The OMTD Program provides an OPOS-compliant application interface to MagTek products and works on Windows 95, 98, ME, NT, 2000, and XP.  OMTD is in the form of a set of ActiveX controls (COs) and a Service Object (SO).

OMTD is the OPOS (OLE for Retail POS) Support for MagTek Devices.  It contains the Control Objects for the MICR, MSR, PINPad, and Line Display device classes, and a Service Object.

The OMTD extensions are installed as part of the MTD installation package.  When installing the MTD drivers, you have the option to include OPOS support.  Refer to the MTD Programming Manual (99875125) for complete installation information.

Part Number	Medium

30037385	MTD/OMTD Installation Package for Windows 95/98/ME/NT/2000/XP (CD)

99510030	MTD/OMTD Installation Package for Windows 95/98/ME/NT/2000/XP (WEB)

## Features

- OMTD is a set of COM objects that act as an extension to the MTD driver and provide an OPOS-compliant application interface to MagTek products.

- Each control consists of a control object (CO) and a service object (SO).  The CO is an ActiveX control that exposes to applications a set of properties, methods and events defined by OPOS for a specific device class (e.g., MICR devices, PINPads, line displays, Magnetic Stripe Readers (MSR), etc.).

- The SO is a local in-process OLE Automation server (in a DLL) that is used by a CO to implement the OPOS-prescribed functionality for a specific device.  The SO performs this functionality by sending one or more commands to the MTD driver using the Win32 File IO.

- In addition to the OPOS-specific functionality, each object exposes the OLE-specific interfaces that make the control Microsoft compliant.

## Requirements

Each control provides the following functionality, to the degree supported by the particular device class.

- Each CO and SO provides self-registration functionality.

- Each CO implements the following standard OLE control interfaces thereby making the control Microsoft OLE compliant: IDispatch, IViewObject2, IOleInPlaceObject, IOleObject, IPersistStorage, IDataObject, and IProvideClassInfo.

- Exposes OPOS-specific device class methods and properties through the IDispatch interface.

- Each CO implements all OPOS-specific functionality for a specific device class as defined by the OPOS Specification.

- A CO will only support MagTek SO(s).

- The SO implements the following standard OLE interfaces: IUnknown, IClassFactory, and IDispatch.

- The SO implements a union of all supported OPOS device class interfaces.

- The SO implements the OPOS functionality by sending commands to the MTD driver using the Win32 File IO API.

### Interfacing to Applications

The OPOS Specification defines a common architecture for interfacing Windows applications with a variety of POS devices.  The CO is loaded and created by the host application or container class whenever it needs to interact with the supported device.  If an application needs to access a combo device (one that supports multiple device classes), the application is required to create and open several different control objects, one for each base class functionality that the device supports.

### Interfacing to the Device

The CO loads and creates a SO in response to an application requesting a device to be opened.  The CO invokes methods on the SO to request implementation of OPOS-specific functionality.  In response, the SO sends one or more commands to the MTD driver using the Win32 File IO API to access the device functionality.

### Supported Device Classes

The following OPOS device classes are supported by the SO:

- MSR (Magnetic Stripe Reader, e.g., Port Powered Swipe Reader, MiniWedge Swipe Reader)

- MICR (Magnetic Ink Character Recognition Check Reader, e.g., MICR Plus, Mini MICR)

- PINPad (e.g., IntelliPIN)

- Line Display (e.g., IntelliPIN)

### Operation

The requirements for operation are as follows:

- Computer system: Intel Pentium-based PC or better

- Operating system: Microsoft Windows 95/98/ME/NT/2000/XP

- Environment: Win32

- Packaging: ActiveX control (.OCX) for OMTD CO, COM in-process server (.DLL) for OMTD SO

- Device access: OMTD accesses the device through existing MTD drivers.

## Compatibility

Each of the OMTD controls is designed to be compatible with release 1.04 of the OPOS Specification and work with any containing application or container that implements the standard OLE mechanisms of creation and binding.

The common service object is designed to be compatible with the 1.05 version of the MTD driver or later.   The SO will function with earlier versions of MTD, but not all functionality may be supported (e.g., data parsing).

It must be noted that the MTD driver itself does not have any knowledge about OPOS.  This gives the ability to modify the OMTD controls without having to modify the MTD drivers and visa versa.

MTD will auto-configure OPOS parameters when it is installed and when any changes are made to the device (e.g., add, remove, friendly name change, etc.).

## Configuration

The OPOS specification does not provide support for or prescribe mechanisms for configuration of OPOS controls.  To provide a service to the user, the configuration of the OMTD controls will be integrated with the MTD class installer.

The OPOS configuration for MagTek devices is provided in a separate DLL that is invoked by both the OMTD setup application and the MTD class installer when they want to modify the OPOS configuration for a device.

## Reference Documents

1.	MagTek Device Drivers for Windows, Technical Reference Manual (P/N 99875125)

2.	OLE for Retail POS, Application Programmer’s Guide, Release 1.4, September 23, 1998,

# International Standard, other OLE/ActiveX compliant 32-bit operating system

3.	OLE for Retail POS, Control Programmer’s Guide, Release 1.4, International Standard, September 24, 1998, Windows 95/98, Windows NT, or other OLE/ActiveX compliant 32-bit operating system

4.	Header files for VC++ and VB

5.	OLE Controls Inside Out, Adam Denning, Microsoft Press, 1995

# Section 2.  Installation

MagTek Device Drivers (MTD) must be installed before installing the OMTD.  Refer to MagTek Device Drivers for Windows, Technical Reference Manual, P/N 99875125.

## OMTD Installation Notes

The OMTD extensions to the MTD Drivers are installed as part of the MTD installation package.  When installing the MTD drivers, check the OPOS Support option at the top of the list.

Selecting the OPOS Support option triggers the installation of all of the OMTD controls.  It also copies all CO and SO packages, and adds registry entries under the OPOS service provider key.  Additionally, all of the installed MTD devices will be configured for OPOS operation.  Each MTD driver will be mapped to the service object for all device classes supported by the particular device.

Note

When installing the OPOS Support on Windows 2000 and XP, you will need to manually configure the devices by using the OMTDCFG configuration utility.  See Modifying and Removing Devices below for more information.

## Registering OLE Programmatic ID Alias for OPOS Control Object

The OPOS specification states that the OLE Programmatic IDs for OPOS control objects should be OPOS.xxx where xxx specifies the device class of the control object (e.g., MSR, MICR, PINPad, etc).  The result of this requirement is that only one control object of a specific device class can be registered at a single time.

By default, the OMTD installation registers aliases for the control objects’ OLE programmatic ID, as required by the OPOS specification.  The registered aliases are:

- MSR Control Object		(	OPOS.MSR

- MICR Control Object		(	OPOS.MICR

- PINPad Control Object		(	OPOS.PINPad

- Line Display Control Object	(	OPOS.LineDisplay

If it is desired to use more than one control object of a specific device class at a time, the alias registration can be bypassed by typing a:\setup c in step #4 below.

When the alias registration is bypassed, the control objects are registered under the following OLE programmatic IDs:

- MSR Control Object		(	MAGTEK.OPOS.MSR

- MICR Control Object		(	MAGTEK.OPOS.MICR

- PINPad Control Object		(	MAGTEK.OPOS.PPAD

- Line Display Control Object	(	MAGTEK.OPOS.LDSP

## Modifying and Removing Devices

After the OMTD Controls are installed, the configuration utility (OMTDCFG.EXE) can be used to update/remove OPOS configuration for installed MagTek devices.   It is copied to the C:\ProgramFiles\MagTek\MTDInstall Folder when the OMTD controls are installed.  OMTDCFG.EXE is a Win32 console application that has the following usage:

omtdcfg [/|-][option] [class flag]

The [option] parameter can be one of the following:

- c , C	(	Configure OPOS support for installed MagTek devices

- d , D	(	Remove OPOS support for configured MagTek devices

- l , L	(	List currently configured MagTek devices

- ?		(	Display usage help

The [class flag] parameter gives the option to select specific device classes to configure, remove, or list.  It is a bit flag that can be one or more of the following:

- <empty>  	(	Perform operation for all device classes listed below

- 0x01	(	Perform operation for MSR device class

- 0x02	(	Perform operation for MICR device class

- 0x04	(	Perform operation for PIN Pad device class

- 0x08	(	Perform operation for Line Display device class

The configuration utility should be run after MagTek devices are installed, removed, or modified in Windows NT/2000/XP.

The configuration utility should be run from the DOS command line so that its output may be seen.

Examples:

omtdcfg -C 0x02 [configure MICR devices]

omtdcfg -L 0x03 [list MICR & MSR devices]

After this, a window listing all of the configured devices will be shown, as indicated below.

# Section 3.  Implementation notes

The following sections define specifics of the OMTD implementation of the OPOS controls.

## Single Service Object

The OMTD product implements a slight deviation from the OPOS Specification.  The OPOS Specification specifies that there is a separate control object for each device class and separate service object for each device model. OMTD conforms to the idea of a separate control object per device class, but it diverges from the specification in that OMTD contains a single service object that is used for all device models.

The reasoning behind the separate service object idea is that each device has its own interface (i.e., set of commands) and communication channel (e.g., RS-232 or keyboard) which requires different implementations of the OPOS functionality.

The OMTD product contains only one service object, the common service object, because the MTD driver handles the data medium and the transport protocol to the device, providing uniform access to the device regardless of the type of connection and device model.

## Potential Problems in Windows 95/98

The MTD property sheet (settings) in Windows 95/98 has an additional check box that is used to enable or disable OMTD for that device. When a new device is installed, the box is checked by default if OMTD is installed.

When the box is checked, the class installer creates and maintains a registry entry that maps the device name to the SO for each device class supported by the device.  The registry entry is made up of the friendly name for the device (e.g., "micr+") and the device class (e.g., msr) separated by a period.  An example is: "Micr+.msr".

When the state of the box is changed from checked to unchecked or the device is removed from the system, the class installer removes the device’s registry entries for each supported device class.

## Modifying OMTD Device Configuration

The OMTD Service Object accepts per-device parameterization from the registry under the following path:

HKLM\Software\OLEForRetail\ServiceInfo\MagTek\Devices\<device friendly name>

The following value is currently supported for each device:

| Name | Type | Description |
| --- | --- | --- |
| msr.enable_sentinels | REG_DWORD | When set to 1, the OMTD MSR Control includes start and end sentinels with the TrackXData properties. The default value is 0 (disabled). |

When OMTD is installed or reconfigured, the device configuration, as described above, is reset to the default values for each device.

## Opening the device

The device name that should be provided on the Open method for the control is made up of the friendly name for the device and the device class for which the open method is being called.  It has the following format:

<device friendly name>.<device class>

The table below shows the legal combinations of <device friendly names> and <device class>.

|  | Device Classes |
| --- | --- |
| Default Friendly Name | Msr | Micr | Pinp | Ldsp |
| IntelliPIN RS-232 | X |  | X | X |
| IntelliPIN Wedge | X |  | X | X |
| IntelliPIN MICR+ Aux | X |  | X | X |
| Mag-Wedge | X |  |  |  |
| MiniWedge | X |  |  |  |
| MICR+ | X | X |  |  |
| Mini MICR RS-232 | X | X |  |  |
| Mini MICR Wedge | X | X |  |  |
| MT-85 | X |  |  |  |
| MT-95 | X |  |  |  |
| Port-Powered Swipe reader | X |  |  |  |
| Port-Powered Insert reader | X |  |  |  |

For example, the OPOS device names for MICR+ with an MSR is "micr+.micr" and "micr+.msr".

## Registering OLE Programmatic ID Alias for OPOS Control Object

The OPOS specification states that the OLE Programmatic IDs for OPOS control objects should be OPOS.xxx where xxx specifies the device class of the control object (e.g., MSR, MICR, PINPad, etc).  The result of this requirement is that only one control object of a specific device class can be registered at a single time.

By default, the OMTD installation registers aliases for the control objects’ OLE programmatic ID, as required by the OPOS specification.  The registered aliases are:

- MSR Control Object		(	OPOS.MSR

- MICR Control Object		(	OPOS.MICR

- PINPad Control Object		(	OPOS.PINPad

- Line Display Control Object	(	OPOS.LineDisplay

When the alias registration is bypassed, the control objects are registered under the following OLE programmatic IDs:

- MSR Control Object		(	MAGTEK.OPOS.MSR

- MICR Control Object		(	MAGTEK.OPOS.MICR

- PINPad Control Object		(	MAGTEK.OPOS.PPAD

- Line Display Control Object	(	MAGTEK.OPOS.LDSP

When the OMTD controls are uninstalled, the registered aliases are removed only if they still refer to an OMTD control object meaning that another OPOS control has not been installed after the OMTD controls were installed.

## Device Power Reporting

The OMTD controls do not support the optional power reporting capability described in the OPOS Specification.  This is due to the fact that MagTek devices and MTD do not report power events.

## Saving Device Settings Across Claim/Release

The OPOS Specification defines that settable device characteristics are saved and restored for each application that accesses the device.  The complexity of supporting this functionality does not justify the marginal benefit provided to applications.  If MagTek foresees frequent simultaneous access of a device from multiple applications, this feature may be added later.

## Error Processing

### Reporting

The SO will display a message box if it receives a property request containing an invalid PropIndex.  These types of errors should be found during development, testing, or staging of the containing application prior to rollout to a customer.  This type of error reporting is recommended by the OPOS Specification.

### Incompatibility Issues

If the control object determines that the specified service object is not supplied by MagTek or does not implement the required device class methods, it will fail the Open method.  The CO determines if the SO is supplied by MagTek by querying a private property on the SO.  However, the SO should work with other COs by specification.

The minimally required device class methods are those methods that are common to all device classes.  Based on the service object version, one or more device class-specific methods may also be required.

The PINPad CO will fail the Open method if the OPOS version of the SO is less than 1.3.  This is because the PINPad device class did not exist with prior versions of OPOS.

The SO will fail its OpenService method if it fails to bind to the SOxxx event handlers of the CO.

# Section 4.  Control Objects

This section defines the interfaces, properties, and methods exposed or used by the OMTD control objects.  In the tables that follow, in the “Access” column, “R” indicates that the property is Read Only, “R/W” indicates that the property can be modified.

## Common Interfaces

The following sections describe the interfaces, methods, and properties that are common to all OMTD control objects.

### OLE Interfaces

Each OMTD control object implements the following standard OLE interfaces: IUnknown, IClassFactory, IDispatch, IViewObjectEx, IViewObject2, IViewObject, IOleInPlaceObjectWindowless, IOleInPlaceObject, IOleWindow, IOleInPlaceActiveObject, IOleControl, IOleObject, IPersistStreamInit, IPersist, IConnectionPointContainer, ISpecifyPropertyPages, IQuickActivate, IPersistStorage, IDataObject, IProvideClassInfo, and IProvideClassInfo2.  See the OLE documentation for detailed descriptions of these interfaces.

(See Section 1, Reference Documents, numbers 2, 3, and 4.)

### Event Methods

The following event methods are implemented by the containing application via its IDispatch interface.  These event methods are also implemented by the CO to receive event notifications from the SO except they are preceded with SO and do not have Event in their name (e.g., DataEvent ( SOData)

void DataEvent (LONG Status)

Fired to present input data from the device to the application. The actual input data is placed in one or more device-specific properties.

The Status parameter contains the input status.  Its value is device class-dependent, and may describe the type or qualities of the input.

void DirectIOEvent (LONG EventNumber, LONG *pData, BSTR *pString)

Fired by a Service Object to communicate directly with the application.  This event provides a means for a Service Object to provide events to the application that are not otherwise supported by the Control Object.

void ErrorEvent	(LONG ResultCode, LONG ResultCodeExtended,

LONG ErrorLocus, LONG *pErrorResponse)

Fired when an error is detected and the Control’s State transitions into the error state.

void OutputCompleteEvent (LONG OutputID)

Fired when a previously started asynchronous output request completes successfully.  The OutputID parameter indicates the ID number of the asynchronous output request that is complete.

void StatusUpdateEvent (LONG Status)

Fired when a Control needs to alert the application of a device status change.  The Status parameter is for device class-specific data, describing the type of status change.  When a device is enabled, the Control may fire initial StatusUpdateEvents to inform the application of the device state.

### Common Properties

The following properties are common to all OMTD control objects.  Most properties are initialized to their default values after a successful call to the Open method.  If a property has not been initialized, its default value will be “[Error]” for BSTR properties, 0 for numeric properties and FALSE for Boolean properties.  See the OPOS Specification for more information.

It is the application’s responsibility to determine what properties the CO supports by querying the corresponding capability (e.g. CapXXX) property.  If an unsupported property is accessed that does not have a corresponding capability property, the return status will be OPOS_E_ILLEGAL.

| Property Name | Access | Type | Description |
| --- | --- | --- | --- |
| AutoDisable | R/W | BOOL | Set to TRUE if application wants to receive and process only one input at a time. The default is FALSE. |
| BinaryConversion | R/W | LONG | Format in which characters are placed into BString arguments. The default is OPOS_BC_NONE. |
| CapPowerReporting | R | LONG | Identifies the reporting capabilities of the device. |
| CheckHealthText | R | BSTR | Holds the results of the most recent call to the CheckHealth method. |
| Claimed | R | BOOL | If TRUE, the device is claimed for exclusive access. The device must be claimed before accessing the device methods and properties and before events are fired to the application. The default is FALSE. |
| ControlObjectDescription | R | BSTR | String identifying the CO and the company that produced it (e.g., “MSR OPOS Control, © 1999 MagTek, Inc.”). |
| ControlObjectVersion | R | LONG | Control object version number. |
| DataCount | R | LONG | Number of enqueued data events at the control. The default is 0. |
| DataEventEnabled | R/W | BOOL | When TRUE, a DataEvent is delivered as soon as input data is enqueued. The default is FALSE. |
| DeviceDescription | R | BSTR | String identifying the device (e.g., MICR Plus). |
| DeviceEnabled | R/W | BOOL | When TRUE, the device is placed in an operational state. When FALSE, any input is discarded and output operations are disallowed. The default is FALSE. |
| DeviceName | R | BSTR | Identifies the device (e.g., friendly name of the device). |
| FreezeEvents | R/W | BOOL | When TRUE, the control will not deliver events. The default is FALSE. |
| OutputID | R | LONG | Holds the identifier of the most recently started asynchronous output. |
| PowerNotify | R/W | LONG | Contains the type power notification selection made by the application. The default is OPOS_PN_DISABLED. |
| PowerState | R | LONG | Contains the current power condition, if it can be determined. The default is OPOS_PS_UNKNOWN. |
| ResultCode | R | LONG | Result code of the most recently invoked method. |
| ResultCodeExtended | R | LONG | Contains extended result information when ResultCode is set to OPOS_S_EXTENDED. |
| ServiceObjectDescription | R | BSTR | String identifying the service object supporting the device and the company that produced it (e.g., “OPOS Common Service Object, © 1999 MagTek, Inc.”). |
| ServiceObjectVersion | R | LONG | Service object version number. |
| State | R | LONG | Contains the current state of the control. |

Common Methods

The following methods are common to all OMTD control objects.

LONG Open (BSTR DeviceName)

Call to open a device for subsequent I/O.

When the Open method is successful, it sets the properties Claimed, DeviceEnabled, and FreezeEvents, as well as descriptions and version numbers of the OPOS software layers (i.e. CO and SO).  Additional class-specific properties may also be initialized.

LONG Close 0

Called to release the device and its resources.  If the DeviceEnabled property is TRUE, then the device is first disabled.  If the Claimed property is TRUE, then exclusive access to the device is first released.

LONG Claim (LONG Timeout)

Called to acquire exclusive access to the device. The Timeout parameter gives the maximum number of milliseconds to wait for exclusive access to be satisfied.  If zero, the method attempts to claim the device, then returns the appropriate status immediately.  If OPOS_FOREVER (-1), the method waits as long as needed until exclusive access is satisfied.

LONG Release ()

Call this method to release exclusive access to the device.  If the DeviceEnabled property is TRUE and the device is an exclusive-use device, then the device is first disabled.

LONG CheckHealth (LONG Level)

Called to test the state of a device.  A text description of the results of this method is placed in the CheckHealthText property.  The CheckHealth method is always synchronous.

LONG ClearInput ()

Called to clear all device input that has been buffered.  Any data events or input error events that were enqueued – usually waiting for DataEventEnabled to be set to TRUE and FreezeEvents to be set to FALSE – are also cleared.

LONG ClearOutput ();

Called to clear all device output that has been buffered.  Also, when possible, halts outputs that are in progress.  Any output error events that were enqueued – usually waiting for FreezeEvents to be set to FALSE – are also cleared.

LONG DirectIO (LONG Command, LONG* pData, BSTR* pString)

Call to communicate directly with the Service Object.

This method provides a means for a Service Object to provide functionality to the application that is not otherwise supported by the standard Control Object for its device class.  Depending upon the Service Object’s definition of the command, this method may be asynchronous or synchronous.

Use of DirectIO will make an application non-portable (e.g., it will not work with service objects developed by other companies).  The application may, however, maintain portability by performing DirectIO calls within conditional code.  This code may be based upon the value of the ServiceObjectDescription, DeviceDescription, or DeviceName property.

## Magnetic Stripe Reader (MSR) Device Class

The following sections describe those properties and methods that are specific to the MSR device class.

### MSR Properties

| Property Name | Access | Type | Description |
| --- | --- | --- | --- |
| AccountNumber | R | BSTR | Account number obtained from the most recently swiped card. |
| CapISO | R | BOOL | If TRUE, the device supports ISO cards. |
| CapJISOne | R | BOOL | If TRUE, the device supports JIS Type-I cards. |
| CapJISTwo | R | BOOL | If TRUE, the device supports JIS Type-II cards. |
| DecodeData | R/W | BOOL | If TRUE, each byte of track data contained within the Track1Data, Track2Data, and Track3Data properties is mapped from its raw format to its corresponding decoded ASCII bit sequence. The default is TRUE. |
| ErrorReportingType | R/W | LONG | Specifies when an error is reported by an ErrorEvent when a card is swiped and one or more of the tracks specified by the TracksToRead property contains data with errors. The default is MSR_ERT_CARD – report errors at a card level. |
| ExpirationDate | R | BSTR | Expiration date as retrieved from the most recently swiped card, as four ASCII decimal characters in the form YYMM. |
| FirstName | R | BSTR | First name obtained from the most recently swiped card. |
| MiddleInitial | R | BSTR | Middle initial obtained from the most recently swiped card. |
| ParseDecodedData | R/W | BOOL | If TRUE, the decoded data contained within the Track1Data and Track2Data properties is further separated into fields for access via various other properties. The default is TRUE. |
| ServiceCode | R | BSTR | Service code obtained from the most recently swiped card. |
| Suffix | R | BSTR | Suffix obtained from the most recently swiped card. |
| Surname | R | BSTR | Surname obtained from the most recently swiped card. |
| Title | R | BSTR | Title obtained from the most recently swiped card. |
| Track1Data | R | BSTR | Contains either the track 1 data from the previous card swipe or an empty string. This property contains the track data between but not including the start and end sentinel characters (refer to msr.enable_sentinels). |
| Track1DiscretionaryData | R | BSTR | Track 1 discretionary data obtained from the most recently swiped card. |
| Track2Data | R | BSTR | Contains either the track 2 data from the previous card swipe or an empty string. |
| Track2DiscretionaryData | R | BSTR | Track 2 discretionary data obtained from the most recently swiped card. |
| Track3Data | R | BSTR | Contains either the track 3 data from the previous card swipe or an empty string. |
| TracksToRead | R/W | LONG | Indicates the track data that the application wishes to have placed into the Track1Data, Track2Data and Track3Data properties following a card swipe. The default is MSR_TR_1_2_3. |

### MSR Methods

The MSR device class does not define any additional methods.

### MICR Device Class

The following sections describe those properties and methods that are specific to the MICR device class.

### MICR Properties

| Property Name | Access | Type | Description |
| --- | --- | --- | --- |
| AccountNumber | R | BSTR | A string containing the account number parsed from the most recently read MICR data. |
| Amount | R | BSTR | A string containing the amount field parsed from the most recently read MICR data. |
| BankNumber | R | BSTR | A string containing the bank number portion of the transit field parsed from the most recently read MICR data. |
| CapValidationDevice | R | BOOL | Indicates if this device also performs validation printing via the POS Printer Control’s slip station. |
| CheckType | R | LONG | A number that represents the type of check parsed from the most recently read MICR data. |
| CountryCode | R | LONG | A number that represents the country of origin of the check parsed from the most recently read MICR data. |
| EPC | R | BSTR | A string containing the Extended Processing Code (“EPC”) field parsed from the most recently read MICR data. The string will contain a single character 0 though 9 if the field is present. If not, the string will be empty (“”). |
| RawData | R | BSTR | A string containing the MICR data from the most recent MICR read. |
| SerialNumber | R | BSTR | A string containing the serial number of the check parsed from the most recently read MICR data. |
| TransitNumber | R | BSTR | A string containing the transit field of the check parsed from the most recently read MICR data. |

### MICR Methods

The MagTek MICR devices do not require processing of the following methods, so they will always return OPOS_SUCCESS.

BeginInsertion(LONG Timeout)

Called to initiate check insertion processing.

EndInsertion()

Called to end check insertion processing.

BeginRemoval(LONG Timeout)

Called to initiate check removal processing.

EndRemoval()

Called to end check removal processing.

## PINPad Device Class

The following sections describe those properties and methods that are specific to the PINPad device class.

### PINPad Properties

| Property Name | Access | Type | Description |
| --- | --- | --- | --- |
| AccountNumber | R/W | BSTR | The account number to be used for the current EFT transaction. |
| AdditionalSecurity Information | R | BSTR | This property may contain additional security/encryption information after a DataEvent event. |
| Amount | R/W | CURRENCY | The amount of the current EFT transaction. |
| AvailableLanguagesList | R | BSTR | This property is a comma-separated string of the languages supported by the pre-defined prompts in the PINPad. |
| AvailablePromptsList | R | BSTR | This property is a comma-separated string of supported values for the Prompt property. |
| CapDisplay | R | LONG | Defines the operations that the Application may perform on the PINPad display. |
| CapKeyboard | R | BOOL | Defines whether the application can obtain input from the PINPad keyboard. |
| CapLanguage | R | LONG | Defines the capabilities that the application has to select the language of pre-defined messages (e.g., English, French, and Arabic). |
| CapMACCalculation | R | BOOL | If TRUE, the PINPad supports MAC calculation. |
| CapTone | R | BOOL | If TRUE, the PINPad has a Tone Indicator. |
| EncryptedPIN | R | BSTR | This property will contain the value of the Encrypted PIN after a DataEvent event. |
| MaximumPINLength | R/W | LONG | The application should set this property to the maximum acceptable number of digits in a PIN. |
| MerchantID | R/W | BSTR | The Merchant ID, as it is known to the EFT Transaction Host. |
| MinimumPINLength | R/W | LONG | The application should set this property to the minimum acceptable number of digits in a PIN. |
| PINEntryEnabled | R | BOOL | The PINPad Control object sets this property to TRUE when an EnablePINEntry method is executed. |
| Prompt | R/W | LONG | This property identifies a pre-defined message to be displayed on the PINPad. |
| PromptLanguage | R/W | LONG | This property specifies the language of the message to be displayed (as specified by the Prompt property). |
| TerminalID | R/W | BSTR | The terminal ID, as it is known to the EFT Transaction Host. |
| Track1Data | R/W | BSTR | Contains either the track 1 data from the previous card swipe or an empty string. |
| Track2Data | R/W | BSTR | Contains either the track 2 data from the previous card swipe or an empty string. |
| Track3Data | R/W | BSTR | Contains either the track 3 data from the previous card swipe or an empty string. |
| TransactionType | R/W | BSTR | The type of the current EFT transaction. |

### PINPad Methods

BeginEFTTransaction(BSTR PINPadSystem, LONG TransactionHost)

This method must be called by the application to inform the PINPad Control of the beginning of an EFT Transaction.  The PINPad Control will perform initialization functions (such as computing session keys). No other PINPad functions can be performed until this method is called.  Set the PINPadSystem to “MDK” or “DUKPT”.

EndEFTTransaction ()

This method must be called by the application to inform the PINPad Control of the end of an EFT Transaction.

EnablePINEntry ()

This method is called by the application to enable PIN Entry at the PINPad device.

When the user has completed the PIN entry operation (either by entering their PIN or by hitting Cancel), a DataEvent event will be fired to provide the encrypted PIN to the application.

ComputeMAC(BSTR InMsg, BSTR* pOutMsg)

This method is called by the application to have the PINPad compute a MAC value and append it to the designated message.  Depending on the selected PINPad Management System, the PINPad may also insert other fields into the message. Note that the ComputeMAC method cannot be used while PINPad input (PIN Entry) is enabled.

VerifyMAC(BSTR Message)

This method is called by the application to have the PINPad verify the MAC value in a message received from an EFT Transaction Host.

UpdateKey(LONG KeyNum, BSTR Key)

This method is used to provide a new encryption key to the PINPad.  It is used only for those PINPad Management Systems in which new key values are sent to the terminal as a field in standard messages from the EFT Transaction Host.

## Line Display Device Class

The following sections describe those properties and methods that are specific to the Line Display LDSP device class.

### LDSP Properties

| Property Name | Access | Type | Description |
| --- | --- | --- | --- |
| CapBlink | R | LONG | Holds the character blink capability of the device. |
| CapBrightness | R | BOOL | If TRUE, the brightness control is supported; otherwise it is FALSE. |
| CapCharacterSet | R | LONG | Holds the default character set capability. |
| CapDescriptors | R | BOOL | If TRUE, then the display supports descriptors; otherwise it is FALSE. |
| CapHMarquee | R | BOOL | If TRUE, the display supports horizontal marquee windows; otherwise it is FALSE. |
| CapICharWait | R | BOOL | If TRUE, the display supports intercharacter wait; otherwise it is FALSE. |
| CapVMarquee | R | BOOL | If TRUE, the display supports vertical marquee windows; otherwise it is FALSE. |
| CharacterSet | R/W | LONG | Contains the character set for displaying characters. |
| CharacterSetList | R | BSTR | A string of character set numbers. |
| Columns | R | LONG | Holds the number of columns for this window. |
| CurrentWindow | R/W | LONG | Holds the current window to which text is displayed. |
| CursorColumn | R/W | LONG | Holds the column in the current window to which the next displayed character will be output. |
| CursorRow | R/W | LONG | Holds the row in the current window to which the next displayed character will be output. |
| CursorUpdate | R/W | BOOL | If TRUE when characters are displayed by the DisplayText or DisplayTextAt method, then CursorRow and CursorColumn will be updated to point to the character beyond the last character output. If FALSE when characters are displayed, then the cursor properties will not be updated. |
| DeviceBrightness | R/W | LONG | Holds the device brightness value, expressed as a percentage between 0 and 100. |
| DeviceColumns | R | LONG | Holds the number of columns on this device. |
| DeviceDescriptors | R | LONG | Holds the number of descriptors on this device. If the capability CapDescriptors is TRUE, then DeviceDescriptors is non-zero; otherwise it is zero. |
| DeviceRows | R | LONG | Holds the number of rows on this device. |
| DeviceWindows | R | LONG | Holds the maximum window number supported by this device. A value of zero indicates that only the device window is supported, and that no windows may be created. |
| InterCharacterWait | R/W | LONG | Holds the wait time between displaying each character with the DisplayText and DisplayTextAt methods. This timer gives a “teletype” appearance when displaying the text. |
| MarqueeFormat | R/W | LONG | Holds the marquee format for the current window. |
| MarqueeRepeatWait | R/W | LONG | Holds the wait time between scrolling the final character or row of the window into its viewport and restarting the marquee with the first or last character or row. The wait time is the specified number of milliseconds. (Note that the timer resolution may reduce the precision of the wait time.) |
| MarqueeType | R/W | LONG | Holds the marquee type for the current window. When not DISP_MT_NONE, the window is in Marquee Mode. |
| MarqueeUnitWait | R/W | LONG | Holds the wait time between marquee scrolling of each column or row in the window. The wait time is the specified number of milliseconds. (Note that the timer resolution may reduce the precision of the wait time.) |
| Rows | R | LONG | Holds the number of rows for this window. |

### LDSP Methods

DisplayText(BSTR Data, LONG Attribute)

The characters in Data are processed beginning at the location specified by CursorRow and CursorColumn, and continue in succeeding columns.

DisplayTextAt(LONG Row, LONG Column, BSTR Data, LONG Attribute)

The characters in Data are processed beginning at the window location specified by the Row and Column parameters, and continuing in succeeding columns.  This method has the same effect as setting the CursorRow to Row, setting CursorColumn to Column, and calling the DisplayText method.

ClearText()

Clears the current window to blanks, sets CursorRow and CursorColumn to zero, and resynchronizes the beginning of the window with the start of the viewport.

ScrollText(LONG Direction, LONG Units)

Scrolls the current window.

SetDescriptor(LONG Descriptor, LONG Attribute)

Sets the state of one of the descriptors, which are small indicators with a fixed label.

ClearDescriptors()

Turns off all descriptors.

CreateWindow	(LONG ViewportRow, LONG ViewportColumn,

LONG ViewportHeight, LONG ViewportWidth,

LONG WindowHeight, LONG WindowWidth)

Creates a viewport over the portion of the display given by the first four parameters.  The window size is given by the last two parameters.  Valid window row values range from (0) to (WindowHeight-1) and column values range from (0) to (WindowWidth-1).

DestroyWindow()

Destroys the current window.  The characters displayed in its viewport are not changed.

CurrentWindow is set to window 0.  The device window and the associated window properties are updated.

RefreshWindow(LONG Window)

Changes the current window to Window, then redisplays its viewport.  Neither the mapping of the window to its viewport nor the window’s cursor position is changed.

## Use Cases

### Using an OMTD Control

Once an OMTD control has been installed and an application has created and linked to it, the first action an application must take on the CO is to call its Open method passing it a device name that is associated with the control object.  The CO locates the corresponding SO and using the system registry and calls CoCreateInstance passing the SO’s Programmatic GUID to create the object.  The CO then binds to the SO’s interfaces and invokes its OpenService method.

The CO initializes its properties as well as descriptions and version numbers of the OPOS control layers.  Additional class-specific properties may also be initialized.

Since several applications may have the same device open at the same time, an application must gain exclusive access to the device by calling the Claim method.  This method must be called before some methods and properties may be accessed.

Before the application can use the device, it must set the DeviceEnabled property to TRUE.  This value brings the device to an operational state, while FALSE disabled the device.  When a device is disabled, any physical input from the device will be discarded until the device is enabled.

An application uses the device by invoking various methods on the CO via the IDispatch interface.

When an application has finished using the device, the Close method should be called to release the device and associated resources.  If the DeviceEnabled property is TRUE, then Close disables the device.  If the Claimed property is TRUE, the Close releases the lock.

Before exiting, an application should close all open OMTD Controls.

## Supported Device Features

The following sections describe the OPOS features that are not supported or partially supported for each device class. The restrictions are based on the functionality of the supported MagTek devices. In some cases, features not supported by the device (e.g., multiple windows in the Line Display) can be implemented by OMTD in software at a later time.

### Common Features

#### Common Properties

| Property Name | Comments |
| --- | --- |
| CapPowerReporting | This property returns OPOS_PR_NONE for all devices because no MagTek devices have power reporting capabilities. |
| Claimed | All devices must be claimed before access will be granted by the control. |
| PowerNotify | This property is initialized to OPOS_PN_DISABLED and the control will fail any attempts to enable this property because it is not supported by any devices. |
| PowerState | This property will always return OPOS_PS_UNKNOWN because CapPowerReporting is OPOS_PR_NONE. |

#### Common Methods

| Method Name | Comments |
| --- | --- |
| CheckHealth | Only OPOS_CH_INTERNAL is supported by the SO. All other levels are mapped to OPOS_CH_INTERNAL. |
| DirectIO | At this time, no commands have been defined for this method. See the Discretionary Features section later in this document for more details. |

#### Common Events

| Event Name | Comments |
| --- | --- |
| DirectIOEvent | Used only if asynchronous DirectIO method is supported. |
| OutputCompleteEvent | This event is not used because all output is performed synchronously for the device classes supported by OMTD. |
| StatusUpdateEvent | This event is not used because the power state reporting capability is not supported and no status update events are defined for the device classes supported by OMTD. |

### MSR Device Class

#### MSR Properties

| Property Name | Comments |
| --- | --- |
| TracksToRead | This property modifies the “trk_enable” property of the MTD driver. |
| DecodeData | This property cannot be set to FALSE because the devices send all track data in decoded format. |

#### MSR Methods

There are no device class-specific methods defined for the MSR class.

### MICR Device Class

#### MICR Properties

| Property Name | Comments |
| --- | --- |
| CapValidationDevice | This property will always be FALSE because the MICR devices do not support validation printing. |
| RawData | This property will contain the check data as returned by the MTD driver (e.g., 6500 format). |

The CheckType and CountryCode properties are set based upon the MICR check status that is returned by the device and provided in the response of the /read command.  The following table describes the values that are stored in the CheckType and CountryCode properties based on the MICR status.  The MICR status values are listed in order of priority that they are returned by the device.

| MICR Status | Description | CheckType Value | CountryCode Value |
| --- | --- | --- | --- |
| 00 | No error, check OK | MICR_CT_PERSONAL | MICR_CC_USA |
| 01 | No MICR Data | MICR_CT_UNKNOWN | MICR_CC_UNKNOWN |
| 03 | Low MICR signal, good read | MICR_CT_PERSONAL | MICR_CC_USA |
| 04 | Check # Error, Bad character in check #, or no check #. | MICR_CT_PERSONAL | MICR_CC_USA |
| 05 | Transit Error | MICR_CT_PERSONAL | MICR_CC_USA |
| 07 | Account Error | MICR_CT_PERSONAL | MICR_CC_USA |
| 08 | Canadian Check | MICR_CT_PERSONAL | MICR_CC_CANADA |
| 09 | Mexican Check | MICR_CT_PERSONAL | MICR_CC_MEXICO |
| 10 | Business Check | MICR_CT_BUSINESS | MICR_CC_USA |
| 11 | Amount field present | MICR_CT_PERSONAL | MICR_CC_USA |

#### MICR Methods

| Method Name | Comments |
| --- | --- |
| BeginInsertion | This method either always returns success or causes a /read check command to be sent to the MTD driver. |
| EndInsertion | This method always returns success. Optionally, it may wait until /read check command completes or the specified timeout expires. |
| BeginRemoval | This method always returns success because the MICR devices do not support its functionality. |
| EndRemoval | This method always returns success. |

### PINPad Device Class

#### PINPad Properties

| Property Name | Comments |
| --- | --- |
| AvailableLanguagesList | This property is not supported because CapDisplay is PPAD_DSP_UNRESTRICTED. |
| AvailablePromptsList | This property is not supported because CapDisplay is PPAD_DSP_UNRESTRICTED. |
| CapDisplay | This property is initialized to PPAD_DSP_UNRESTRICTED, which specifies that the Line Display CO is the interface to the PINPad display. |
| CapLanguage | This property is initialized to PPAD_LANG_NONE because CapDisplay is PPAD_DSP_UNRESTRICTED. |
| CapMACCalculation | This property is always FALSE. MAC calculation is not supported due to security concerns. |
| CapKeyboard | This property is always FALSE. At a later time, access to the keyboard functionality may be added through a POS Keyboard control. |
| CapTone | This property is always FALSE because the IntelliPIN does not have a Tone Indicator. |
| MerchantID | This property is supported, but has no effect on the operation of the device (i.e., no commands are sent to the device). |
| MinimumPINLength | This property is supported, but cannot be modified. The minimum PIN length is based on the current encode mode (M/S or DUKPT). |
| Prompt | This property is not supported because CapDisplay is PPAD_DSP_UNRESTRICTED. |
| PromptLanguage | This property is not supported because CapDisplay is PPAD_DSP_UNRESTRICTED. |
| TerminalID | This property is supported, but has no effect on the operation of the device. |
| TransactionType | Only PPAD_TRANS_DEBIT and PPAD_TRANS_CREDIT options are supported because these are the transaction types supported by IntelliPIN. |

#### PINPad Methods

| Method Name | Comments |
| --- | --- |
| BeginEFTTransaction | The only supported PINPad Management Systems are “M/S” and “DUKPT” – the ones supported by IntelliPIN. |
| ComputeMAC | This function is not supported due to security concerns. |
| VerifyMAC | This function is not supported due to security concerns. |

### Line Display Device Class

#### LDSP Properties

The following table lists those properties that are supported by the Line Display CO.  All other properties are not supported.

| Property Name | Comments |
| --- | --- |
| CapBlink | CAP_CB_NOBLINK |
| CapBrightness | FALSE |
| CapCharacterSet | DISP_CCS_ASCII |
| CapDescriptors | FALSE |
| CapHMarquee | FALSE |
| CapICharWait | FALSE |
| CapVMarquee | FALSE |
| DeviceWindows | 0 (only device window supported) |
| DeviceRows | 2 |
| DeviceColumns | 16 |
| DeviceDescriptors | 0 |
| DeviceBrightness | 100 only |
| CharacterSet | DISP_CS_ASCII only |
| CharacterSetList | 998 |
| CurrentWindow | 0 only |
| Rows | 2 |
| Columns | 16 |
| CursorRow | 0..1 |
| CursorColumn | 0..16 |
| CursorUpdate | TRUE, FALSE |
| MarqueeType | DISP_MT_NONE only |
| MarqueeFormat | DISP_MF_WALK (not used) |
| MarqueeUnitWait | 0 (not used) |
| MarqueeRepeatWait | 0 (not used) |
| InterCharacterWait | 0 (not used) |

#### LDSP Methods

Based on the device features and the capabilities defined above, only the following methods are supported:

| Method Name | Comments |
| --- | --- |
| ClearText | Supported |
| DisplayText | Supported |
| DisplayTextAt | Supported |

# Appendix A.  Glossary

| CO | OPOS Control Object – ActiveX Control that exposes a set of properties, methods, and events to an application for its device class |
| --- | --- |
| COM | Component Object Module |
| Device | Physical MagTek device (e.g., Port Powered Swipe Reader, MICR+, IntelliPIN, etc.) |
| Device class | Category of POS devices that share a consistent set of properties, methods, and events (e.g., MSR, MICR, PINPad, etc.) |
| DLL | Dynamic-Link Library |
| LDSP | Line Display Device (e.g., LCD on IntelliPIN) |
| MICR | Magnetic Ink Character Recognition (Check Reader) |
| MSR | Magnetic Stripe Reader |
| MTD | MagTek Device Driver |
| OLE | Object Linking and Embedding |
| OPOS | OLE for Retail Point of Sale |
| PINPad | PINPad Device Class (PIN Entry Device) |
| SO | OPOS Service Object – COM in-process server that provides the device-specific OPOS functionality |

# Index

A

ActiveX	1

Auto-configure	3

B

BeginEFTTransaction	21

BeginInsertion	19

BeginRemoval	19

C

CheckHealth	16

Claim	16

Claim/Release	11

Class Flag	7

ClearDescriptors	23

ClearInput	16

ClearOutput	16

ClearText	23

Close	15

CO	31

COM	31

COM objects	1

Combo Device	2

Common Events	25

Common Features	25

Common Interfaces	13

Common Methods	15, 25

Common Properties	14, 25

ComputeMAC	21

Configuration	4

Control Objects	13–30

CreateWindow	23

D

DataEvent	13

DestroyWindow	24

Device	31

Device class	31

Device Classes	2

Device Features, Supported

Common Features	25

Device Power Reporting	11

DirectIO	16

DirectIOEvent	13

Discretionary Features	25

DisplayText	23

DisplayTextAt	23

DLL	31

E

EnablePINEntry	21

EndEFTTransaction	21

EndInsertion	19

EndRemoval	19

Error Processing	11

ErrorEvent	14

Event Methods	13

F

Features	1

Features and Specifications	1–4

Friendly Name	9, 10

G

Glossary	31

I

Implementation Notes	9–12

Incompatibility Issues	12

Installation	5

K

KeyNum	21

L

LDSP	31

LDSP Methods	23, 29

LDSP Properties	22, 28

License	iii

Line Display Control Object	6

Line Display Device Class	21, 28

Line Displays	1

LONG Release	16

M

Magnetic Stripe Reader Device Class	17

Methods	15

MICR	1, 31

MICR Control Object	6

MICR Device Class	18, 26

MICR Methods	19, 27

MICR Properties	18, 26

Modifying and Removing Devices	6

Modifying OMTD Device Configuration	9

MSR	1, 31

MSR Control Object	6

MSR Device Class	26

MSR Methods	18, 26

MSR Properties	17, 26

msr.enable_sentinels	10

MTD	3, 31

O

OLE	31

OLE Interfaces	13

OMTD Control, Using	24

OMTDCFG	6, 7

Open	15

Open Method	10

OPOS	31

OPOS Specification	3

OutputCompleteEvent	14

P

PINPad	31

PINPad Control Object	6

PINPad Device Class	19, 27

PINPad Methods	21, 28

PINPad Properties	20, 27

PINPads	1

Potential Problems	9

Power Reporting	11

Properties	14

R

Reference Documents	4

RefreshWindow	24

Registering OLE Programmatic ID Alias for OPOS Control Object	6, 10

Release	16

Requirements	1

S

Saving Device Settings	11

ScrollText	23

Sentinels	10

Service Object	9

SetDescriptor	23

Single Service Object	9

SO	31

StatusUpdateEvent	14

Supported Device Features	25

U

UpdateKey	21

Use Cases	24

Using an OMTD Control	24

V

VerifyMAC	21

# Text boxes

MTD

MagTek Device Drivers  for

Windows 95/98/NT

OMTD

Control Objects (CO)

for

MICR, MSR, PINPad, and Line Display

OMTD

Service Object (SO)

User-Supplied

Control Objects

(CO)