BATCH DOWNLOAD

Batch downloading

User's manual

| BatchDownload_UM_1.doc Version: 1.0.1 May 13, 2002 |  |
| --- | --- |

Table of Contents

A.	Introduction	A-1

B.	Installation	B-1

C.	Using BMidWin and BMidDos	C-1

D.	Using BatchChameleon	D-2

# Introduction

Batch downloading is used for automatic downloading of the keyboard configuration according to the current user or the current application. The MID or TouchMe configuration can be configured on one computer and used on the others. Examples of usage:

- The administrator configures the keyboard and distributes the configuration to all operators. E.g. in POS, the technical administrator changes the application, the keyboards must be reconfigured on all POS systems. Operators are not able to change the configuration.

- Several users use the same keyboard but only one at a time. Each user has his own configuration. When he logs in, the configuration is downloaded to the keyboard.

There are three batch dowload programs:

- BMidDos

- BMidWin

- BatchChameleon

BMidDos and BMidWin are used for downloading the keyboard content. BatchChameleon is used for downloading the Chameleon configuration (images, colors...) without key content. Key content for the Chameleon must be downloaded by BMidWin. BMidDos works in DOS operating system. BMidWin and BatchChameleon work in Windows operating systems.

# Installation

Batch downloading programs are not part of the MidWin installation at the moment. They can be supplied by Tipro on request. To be able to use the batch download programs, install MidWin and copy BmidWin.exe and BatchChameleon.exe to the computer hard drive. You can delete MidWin.exe and other files, except the dll files to save disk space or disable changing the configuration on local computer, but do NOT uninstall MidWin!

# Using BMidWin and BMidDos

The command line should look in the following way:

[Program name] [Layout file name] [COMx]

Program name is BMidWin.exe or BMidDos.exe (the path to the programs should be included. The path may not contain spaces, points...)

Layout file name is the name of the file to be downloaded. File name is the same as the project name. The extension is ‘.bin’. Important note: The file path may not contain spaces, points...

COMx is optional if the serial port should be used for downloading. Replace the x by the com port value (1-32)

Examples:

C:\tipro\BMidDos.exe C:\tipro\layouts\monday.bin

Will download the monday.lay project file to the keyboard through PS2 interface.

C:\tipro\batch\BMidWin.exe C:\tipro\layouts\peter.bin COM1

Will download Peter’s layout through COM1.

Wrong usage (mistakes are marked with bold text):

C:\Program Files\BMidWin.exe C:\Tipro\wronguse.bin

Illegal character in program path

C:\BMidWin\BmidWin.exe C:\My Documents\mylayout.bin

Illegal character in file path

C:\BMidWin\BmidWin.exe C:\tipro\mylayout.lay

Illegal file extension

# Using BatchChameleon

The command line should look in the following way:

[ProgramPath\BatchChameleon.exe] [Download file name] [COMx]

The first parameter contains BatchChameleon.exe and path to the file. The path may NOT contain any spaces, points...

Download file name is the name of the file to be downloaded. File name is the same as the project name. The extension is ‘.chd’. Important note: The file path may not contain spaces, points...

COMx is optional if the serial port should be used for downloading. Replace the x by the com port value (1-32)

Important note: With the BatchChameleon, only the visible part of the chameleon configuration is downloaded. Keys content is NOT downloaded with BatchChameleon. For downloading keys content, BMidWin should be used!

Examples:

C:\tipro\BatchChameleon.exe C:\chameleonproject\skin1.chd

C:\tipro\BatchChameleon.exe C:\chameleonproject\skin1.chd COM1

The second example downloads through the serial port COM1.

Remember to download also the keys content after downloading Chameleon properties.

Wrong usage (mistakes are marked with bold text):

C:\prog files\BatchChameleon.exe C:\My documents\chameleonproject\skin1.chd

Illegal character in the program path and in the file path

C:\tipro\BatchChameleon.exe C:\chameleonproject\skin1.chp

Illegal file extension (chp is the project extension, chd is the download file extension