FORD C-MAX & GRAND C-MAX Specifications

Performance and Economy

| C-MAX |  |  | Fuel consumption l/100 km (mpg) ØØ | Performance Ø |
| --- | --- | --- | --- | --- |
| Engine | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h 0-62 mph (sec) | 50-100 km/h 31-62 mph (sec)* |
| 1.0L EcoBoost petrol 6-speed manual with Auto-Start-Stop | 100 | 117 | 6.2 (45.5) | 4.5 (62.7) | 5.1 (55.3) | 174 (108) | 12.9 | 12.0 |
| 1.0L EcoBoost petrol 6-speed manual with Auto-Start-Stop | 125 | 117 | 6.2 (45.5) | 4.5 (62.7) | 5.1 (55.3) | 187 (116) | 11.4 | 11.8 |
| 1.6L TI-VCT petrol 5-speed manual | 85 | 149 | 8.4 (33.6) | 5.2 (54.3) | 6.4 (44.1) | 165 (102) | 15.9 | 16.4 |
| 1.6L TI-VCT petrol 5-speed manual | 125 | 149 | 8.4 (33.6) | 5.2 (54.3) | 6.4 (44.1) | 188 (116) | 11.8 | 14.5 |
| 1.5L TDCi diesel 6-speed manual | 120 | 110 | 5.1 (55.3) | 3.7 (76.3) | 4.2 (67.2) | 184 (114) | 11.3 | 9.9 |
| 1.5L TDCi diesel 6-speed manual with Auto-Start-Stop | 120 | 105 | 4.7 (60.1) | 3.7 (76.3) | 4.1 (68.9) | 184 (114) | 11.3 | 9.9 |
| 1.5L TDCi diesel 6-speed PowerShift | 120 | 120 | 5.4 (52.3) | 4.1 (68.9) | 4.6 (61.4) | 182 (113) | 12.4 | 7.9 |
| 1.5L TDCi diesel 6-speed PowerShift Auto-Start-Stop | 120 | 115 | 5.0 (56.4) | 4.1 (68.9) | 4.4 (64.2) | 182 (113) | 12.4 | 7.9 |
| 1.5L diesel ECOnetic 6-speed manual with Auto-Start-Stop | 105 | 99 | 4.3 (65.7) | 3.5 (80.7) | 3.8 (74.3) | 184 (114) | 12.1 | 11.3 |
| 1.6L TDCi diesel 6-speed manual | 115 | 117 | 5.4 (52.3) | 4.0 (70.6) | 4.5 (62.8) | 184 (114) | 11.3 | 11.3 |
| 2.0L TDCi diesel 6-speed manual with Auto-Start-Stop | 150 | 114 | 5.0 (56.4) | 4.0 (70.6) | 4.4 (64.2) | 204 (126) | 9.5 | 9.2 |
| 2.0L TDCi diesel 6-speed PowerShift with Auto-Start-Stop | 150 | 124 | 5.5 (51.3) | 4.4 (64.2) | 4.8 (58.9) | 202 (125) | 10.3 | 8.8 |
| 2.0L TDCi diesel 6-speed PowerShift with Auto-Start-Stop | 170 | 124 | 5.5 (51.3) | 4.4 (64.2) | 4.8 (58.9) | 212 (131) | 8.5 | 7.5 |

| GRAND C-MAX |  |  | Fuel consumption l/100 km (mpg) ØØ | Performance Ø |
| --- | --- | --- | --- | --- |
| Engine | Power (PS) | CO2 (g/km) | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h 0-62 mph (sec) | 50-100 km/h 31-62 mph (sec)* |
| 1.0L EcoBoost petrol 6-speed manual with Auto-Start-Stop | 100 | 119 | 6.4 (44.1) | 4.6 (61.4) | 5.2 (54.3) | 172 (106) | 13.7 | 12.7 |
| 1.0L EcoBoost petrol 6-speed manual with Auto-Start-Stop | 125 | 119 | 6.4 (44.1) | 4.6 (61.4) | 5.2 (54.3) | 185 (114) | 12.3 | 12.5 |
| 1.6L TI-VCT petrol 5-speed manual | 125 | 154 | 8.6 (32.8) | 5.5 (51.4) | 6.7 (42.2 | 182 (113) | 12.3 | 14.9 |
| 1.5L TDCi diesel 6-speed manual | 120 | 118 | 5.3 (53.3) | 4.1 (68.1) | 4.6 (61.4) | 180 (111) | 12.3 | 10.1 |
| 1.5L TDCi diesel 6-speed manual with Auto-Start-Stop | 120 | 113 | 4.9 (57.6) | 4.1 (68.1) | 4.4 (64.2) | 180 (111) | 12.3 | 10.1 |
| 1.5L TDCi diesel 6-speed PowerShift | 120 | 129 | 5.9 (47.9) | 4.5 (62.8) | 5.0 (56.4) | 178 (110) | 13.4 | 8.0 |
| 1.5L TDCi diesel 6-speed PowerShift Auto-Start-Stop | 120 | 124 | 5.4 (52.3) | 4.5 (62.8) | 4.8 (58.9) | 178 (110) | 13.4 | 8.0 |
| 1.6L TDCi diesel 6-speed manual | 115 | 129 | 5.8 (48.7) | 4.4 (64.2) | 4.9 (57.6) | 180 (111) | 12.3 | 11.3 |
| 2.0L TDCi diesel 6-speed manual with Auto-Start-Stop | 150 | 119 | 5.2 (54.3) | 4.2 (67.2) | 4.6 (61.4) | 202 (125) | 9.8 | 9.3 |
| 2.0L TDCi diesel 6-speed PowerShift with Auto-Start-Stop | 150 | 129 | 5.6 (50.4) | 4.6 (61.4) | 5.0 (56.4) | 200 (124) | 10.7 | 8.9 |
| 2.0L TDCi diesel 6-speed PowerShift with Auto-Start-Stop | 170 | 129 | 5.6 (50.4) | 4.6 (61.4) | 5.0 (56.4) | 209 (129) | 8.8 | 7.6 |

*In 4th gear. ØFord test figures. ØØThe declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

WEIGHTS C-MAX

|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) | Max. Roof Load [kg] |
| --- | --- | --- | --- | --- | --- | --- |
| 1.0L EcoBoost petrol 6-speed manual 100 PS | 1391 | 1900 | 3100 | 1200 | 695 | 75 |
| 1.0L EcoBoost petrol 6-speed manual 125 PS | 1391 | 1900 | 3100 | 1200 | 695 | 75 |
| 1.6L Ti-VCT petrol 5-speed manual 85 PS | 1374 | 1860 | 2660 | 800 | 685 | 75 |
| 1.6L Ti-VCT petrol 5-speed manual 125 PS | 1374 | 1860 | 2860 | 1000 | 685 | 75 |
| 1.5L TDCi diesel 6-speed manual 95 PS | 1403 | 1915 | 3115 | 1200 | 700 | 75 |
| 1.5L TDCi diesel 6-speed manual 120 PS | 1403 | 1915 | 3115 | 1200 | 700 | 75 |
| 1.5L TDCi diesel 6-speed PowerShift 120 PS | 1472 | 2000 | 3200 | 1200 | 735 | 75 |
| 1.5L diesel ECOnetic 6-speed manual 105 PS | 1405 | 1915 | 2315 | 400 | 400 | 75 |
| 1.6L TDCi diesel 6-speed manual 115 PS | 1390 | 1915 | 3115 | 1200 | 695 | 75 |
| 2.0L TDCi diesel 6-speed manual 150 PS | 1491 | 2050 | 3550 | 1500 | 745 | 75 |
| 2.0L TDCi diesel 6-speed PowerShift 150 PS | 1519 | 2050 | 3550 | 1500 | 750 | 75 |
| 2.0L TDCi diesel 6-speed PowerShift 170 PS | 1519 | 2050 | 3550 | 1500 | 750 | 75 |

WEIGHTS GRAND C-MAX

|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) | Max. Roof Load [kg] |
| --- | --- | --- | --- | --- | --- | --- |
| 1.0L EcoBoost petrol 6-speed manual 100 PS | 1493 | 2150 | 3050 | 900 | 745 | 75 |
| 1.0L EcoBoost petrol 6-speed manual 125 PS | 1493 | 2150 | 3050 | 900 | 745 | 75 |
| 1.5L EcoBoost petrol 6-speed manual 150 PS | 1473 | 2195 | 3495 | 1300 | 735 | 75 |
| 1.5L EcoBoost petrol 6-speed auto 150 PS | 1507 | 2200 | 3500 | 1300 | 750 | 75 |
| 1.5L EcoBoost petrol 6-speed auto 182 PS | 1507 | 2200 | 3500 | 1300 | 750 | 75 |
| 1.5L EcoBoost petrol 6-speed manual 182 PS | 1473 | 2195 | 3495 | 1300 | 735 | 75 |
| 1.6L TI-VCT petrol 5-speed manual 125 PS | 1477 | 2135 | 2885 | 750 | 735 | 75 |
| 1.5L TDCi diesel 6-speed manual 95 PS | 1501 | 2225 | 3425 | 1200 | 750 | 75 |
| 1.5L TDCi diesel 6-speed manual 120 PS | 1501 | 2225 | 3425 | 1200 | 750 | 75 |
| 1.5L TDCi diesel 6-speed PowerShift 120 PS | 1532 | 2250 | 3450 | 1200 | 750 | 75 |
| 1.6L TDCi diesel 6-speed manual 115 PS | 1504 | 2200 | 3400 | 1200 | 750 | 75 |
| 2.0L TDCi diesel 6-speed manual 150 PS | 1577 | 2300 | 4100 | 1800 | 750 | 75 |
| 2.0L TDCi diesel 6-speed PowerShift 150 PS | 1605 | 2300 | 4100 | 1800 | 750 | 75 |
| 2.0L TDCi diesel 6-speed PowerShift 170 PS | 1605 | 2300 | 4100 | 1800 | 750 | 75 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90% fuel levels, subject to manufacturing tolerances and options, etc., fitted. Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing. Nose weight limit is a maximum of 75 kg on all models except for 2.0 TDCi engines which are 90 kg. Gross Train Mass includes trailer weight

DIMENSIONS

| Exterior (mm) | C-MAX | GRAND C-MAX |
| --- | --- | --- |
| Overall length | 4379 | 4519 |
| Overall width with/folded/without mirrors | 2067 / 1858 / 1828 | 2067 / 1858 / 1828 |
| Overall max height | 1610 | 1642 (1694 with roof rails) |
| Track front min/max depending on tyre size and wheel offset | 1543 / 1557 | 1543 / 1557 |
| Track rear min/max | 1554 / 1569 | 1554 / 1569 |
| Interior (mm) |  |  |
| Front headroom | 1041 | 1038 |
| Front max legroom (mid-height rearmost seating position) | 1083 | 1083 |
| Front shoulder room | 1422 | 1422 |
| 2nd row headroom | 981 | 988 |
| 2nd row legroom (nominal with front row in 95% SAE position) | 916 | 864 (864-966) |
| 2nd row shoulder room | 1402 | 1427 |
| 3nd row headroom | N/A | 937 |
| 3nd row legroom (nominal with front row in 95% SAE position) | N/A | 784 |
| 3nd row shoulder room | N/A | 1190 |
| Luggage capacity (litres)‡ | C-MAX | 7-SEAT / 5-SEAT |
| 7-seat mode (laden to package tray, with mini spare) | N/A | 65 / N/A |
| 7-seat mode (laden to package tray, with tyre repair kit) | N/A | 92 / N/A |
| 7-seat mode (laden to roof, with mini spare) | N/A | 88 / N/A |
| 7-seat mode (laden to roof, with tyre repair kit) | N/A | 115 / N/A |
| 5-seat mode (laden to package tray, with mini spare, 2nd row in rearmost position) | 432 | 448 / 520 |
| 5-seat mode (laden to package tray, with tyre repair kit, 2nd row in rearmost position) | 471 | 475 / 600 |
| 5-seat mode (laden to roof, with mini spare, 2nd row seats in rearmost position) | 627 | 728 / 800 |
| 5-seat mode (laden to roof, with tyre repair kit, 2nd row in rearmost position) | 666 | 755 / 880 |
| 2-seat mode (laden to roof, with mini spare, 1st row in 95% position 24 degree back angle) | 1684 (2nd row folded) | 1715 / 1787 |
| 2-seat mode (laden to roof, with tyre repair kit, 1st row in 95% position 24 degree back angle) | 1723 (2nd row folded) | 1742 (2nd row not folded) / 1867 |
| Luggage Compartment Dimensions (mm) |  |  |
| Load opening height max | 816 | 853/920 |
| Load opening width max | 1030 | 1030/1030 |
| Max loading height | 986 | 843/1053 |
| Luggage Compartment Dimensions (mm) |  |  |
| Loading width between wheelhouses | 1030 | 1030/1030 |
| Loading length at floor to third row | N/A | 294 |
| Loading length at floor to 2nd row (min / max) | 870 | 976 - 1126/1013 -1163 |
| loading length to first row | 1706 | 1758/1780 |
| Lift over height at curb load condition (unladen) | 601 | 675/609 |

| Fuel tank capacity (litres) | C-MAX | GRAND-C-MAX |
| --- | --- | --- |
| Petrol | 55 | 60 |
| Diesel | 53 / 60** | 60 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

**2.0 Duratorq TDCi engine only

STEERING AND SUSPENSION

|  | C-MAX | GRAND C-MAX |
| --- | --- | --- |
| System | Rack and Pinion with Electronic Power Assisted Steering (EPAS) |
| Turning circle – kerb-to-kerb (m) | 10.7 | 11.2 |
| Turning circle – wall-to-wall (m) | 11.1 | 11.6 |

CHASSIS

| Front suspension | Independent MacPherson struts with offset coil spring over gas filled damper units and lower L-arms with optimised front rubber bushings and rear hydro-bush mounted on separate reinforced cross-member sub-frame, anti-roll bar. |
| --- | --- |
| Rear suspension | Fully independent multi-link Control Blade with large dampers. Rear damper with dual path body mounts. Anti-roll-bar connected to spring links. |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Dual circuit, diagonally split, hydraulically operated front and rear with disc/drum brakes. Vacuum servo assisted with four-channel ABS and electronic brake distribution (EBD) |
| Disc/Drum dimensions (mm) | 278 x 25 300 x 25* | 280 x 11 |

* 2.0-litre TDCi and Grand C-MAX

WHEELS & TYRES

|  | Wheels | Tyres |
| --- | --- | --- |
| Standard | Steel: 16 X 6.5-inch Alloy: 16 X 7-inch | 205/55-R16 215/55-R16 |
| Optional | Alloy: 17 X 7-inch Alloy: 18 X 8-inch | 215/50-R17 235/40-R18 |

ENGINE DATA

|  |  | 1.0-litre EcoBoost petrol (100, 125 PS) | 1.6-litre Ti-VCT petrol (85, 120 PS) |
| --- | --- | --- | --- |
| Type |  | Inline three cylinder turbo petrol direct fuel injection and Ti-VCT, transverse | Inline four cylinder petrol with Ti-VCT, transverse |
| Displacement | cm3 | 998 | 1596 |
| Bore | mm | 71.9 | 79.0 |
| Stroke | mm | 82.0 | 81.4 |
| Compression ratio |  | 10.0:1 | 11.0:1 |
| Max power | PS (kW) | 100 (74) | 125 (92) | 85 (63) | 120 (88) |
|  | at rpm | 6000 | 6000 | 6000 | 6000 |
| Max torque | Nm | 170 | 170 | 141 | 159 |
|  | at rpm | 1400-4000 | 1400-4500 | 2500 | 4000 |
| Valve gear |  | DOHC with 4 valves per cylinder, twin independent variable cam timing | DOHC with 4 valves per cylinder, twin independent variable cam timing |
| Cylinders |  | 3 in-line | 4 in-line |
| Cylinder head |  | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast iron | Cast aluminium |
| Camshaft drive |  | Low friction Belt-in-Oil with dynamic tensioner | Timing belt with dynamic tensioner |
| Crankshaft |  | Cast iron, 6 counterweights, 4 main bearings | Cast iron, 4 counterweights, 5 main bearings |
| Engine management |  | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC Software | Siemens ECM EMS2101 16 Bit |
| Fuel injection |  | High pressure direct fuel injection with 6 hole injectors | Electronic port fuel injection |
| Emission level |  | Euro Stage 6 | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Continental low inertia turbo | n/a |
| Lubrication system |  | Electronically controlled variable displacement oil pump for improved fuel economy | Pressure-fed lubrication system with full flow oil filter |
| System capacity with filter | litres | 4.1 | 4.1 |
| Cooling system |  | Split cooling system with 2 thermostats | Water pump with thermostat and valves |
| System capacity incl heater | litres | 5.8 | 5.5 |
| ENGINE DATA |  | 1.0-litre EcoBoost petrol (100, 125 PS) | 1.6-litre Ti-VCT petrol (85, 120 PS) |
| Transmission |  | Durashift 6-speed (B6) manual | Durashift five-speed (iB5) manual |
| Gear ratios | 6th 0.622 5th 0.738 4th 0.919 3rd 1.258 2nd 2.048 1st 3.727 Reverse 3.818 Final Drive 4.25 | 5th 0.878 4th 1.108 3rd 1.414 2nd 2.045 1st 3.583 Reverse 3.818 Final Drive C-MAX 4.049 Grand C-MAX 4.067 |

DIESEL ENGINES

|  |  | 1.5-litre TDCi diesel (120 PS) | 1.6-litre TDCi diesel (115 PS) | 2.0L TDCi diesel (150, 170 PS) |
| --- | --- | --- | --- | --- |
| Type |  | Inline four cylinder turbocharged diesel | Inline four cylinder turbo diesel, transverse | Inline four cylinder turbocharged diesel |
| Displacement | cm3 | 1499 | 1560 | 1997 |
| Bore | mm | 73.5 | 75.0 | 85.0 |
| Stroke | mm | 88.3 | 88.3 | 88.0 |
| Compression ratio |  | 16:1 | 16:1 | 16:1 |
| Max power | PS (kW) | 120 (88) | 115 (84) | 150 (110) | 170 (125) |
|  | at rpm | 3600 | 3800 | 3500 | 3500 |
| Max torque | Nm | 270 | 215 | 370 | 400 |
|  | at rpm | 1750-2500 | 1750 | 2000-2500 | 2000-2500 |
| Valve gear |  | SOHC with 2 valves per cylinder | DOHC with 2 valves per cylinder | DOHC with 4 valves per cylinder |
| Cylinders |  | 4 in line | 4 in line | 4 in line |
| Cylinder head |  | Cast aluminium | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast aluminium | Cast aluminium | Cast aluminium |
| Camshaft drive |  | Timing belt (crankshaft to intake) with dynamic tensioner; Intake to exhaust chain with hydraulic tensioner | Timing belt (crankshaft to intake) with dynamic tensioner; Intake to exhaust chain with hydraulic tensioner | Belt driven cams with primary drive tensioner |
| Crankshaft |  | Steel, 8 counterweights, 5 main bearings | Cast steel, 8 counter- weights, 5 main bearings | Steel, 8 counterweights, 5 main bearings |
| Engine management |  | Ford Common Rail Diesel Engine Management System | Ford Common Rail Diesel Engine Management System | Ford Common Rail Diesel Engine Management System |
| DIESEL ENGINES |  | 1.5-litre TDCi diesel (120 PS) | 1.6-litre TDCi diesel (115 PS) | 2.0L TDCi diesel (150, 170 PS) |
| Fuel injection |  | High pressure direct fuel injection with 8 hole injectors | Common rail direct fuel injection; 1600 bar injection pressure; 7-hole piezo-electric injectors | High pressure direct fuel injection with 8 hole injectors |
| Emission control |  | Oxidation catalyst, water cooled EGR and standard cDPF | Oxidation catalyst, water cooled EGR and standard cDPF | Oxidation catalyst, water cooled EGR and standard cDPF |
| Emission level |  | Euro Stage 6 | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Honeywell VGT | Garrett fixed geometry turbocharger | Honeywell VGT |
| Lubrication system |  | Crankshaft nose driven oil pump | Pressure-fed lubrication system with full flow oil filter | Crankshaft nose driven oil pump |
| System capacity with filter | litres | 3.8 | 3.8 | 5.7 |
| Cooling system |  | Block mounted centrifugal mechanical water pump and mechanical thermostat. Head mounted water outlet connector with ECT sensor. | Water pump with thermostat and valves, with thermal management system | Block mounted centrifugal mechanical water pump and mechanical thermostat. Head mounted water outlet connector with ECT sensor. |
| System capacity incl heater | litres | 5.8 | 5.8 | 6.3 |
| Transmission |  | Durashift 6-speed (B6) manual | Automatic 6-speed (MPS6) PowerShift | Durashift 6-speed (B6) manual | Automatic 6-speed (MPS6) PowerShift | Manual 6-speed (MMT6) |
| Gear ratios | 6th 0.622 5th 0.738 4th 0.919 3rd 1.258 2nd 2.048 1st 3.727 Reverse 3.818 Final Drive 3.61 | 6th 0.756 5th 0.943 4th 0.829 3rd 1.194 2nd 1.952 1st 3.583 Reverse 4.843 Final Drive 4.067 | 6th 0.622 5th 0.738 4th 0.919 3rd 1.258 2nd 2.048 1st 3.727 Reverse 3.818 Final Drive 3.095 | 6th 0.756 5th 0.943 4th 0.829 3rd 1.194 2nd 1.864 1st 3.583 Reverse 4.843 Final Drive 3.933 | 6th 0.737 5th 0.886 4th 0.816 3rd 1.156 2nd 1.864 1st 3.583 Reverse 1.423 Final Drive 3.688 |

POWER AND TORQUE CURVES

1.0-litre EcoBoost 100 PS

1.0-litre EcoBoost 125 PS

1.6-litre Ti-VCT 85 PS

1.6-litre Ti-VCT 125 PS

1.5-litre TDCi diesel 120 PS

1.6-litre TDCi 115 PS

2.0-litre TDCi diesel 150 PS

2.0-litre TDCi diesel 170 PS

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

# # #

About Ford Motor Company

Ford Motor Company, a global automotive industry leader based in Dearborn, Michigan manufactures or distributes automobiles across six continents. With about 187,000 employees and 62 plants worldwide, the company’s automotive brands include Ford and Lincoln. The company provides financial services through Ford Motor Credit Company. For more information regarding Ford and its products worldwide, please visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 47,000 employees at its wholly owned facilities and approximately 66,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 23 manufacturing facilities (12 wholly owned or consolidated joint venture facilities and 11 unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

| Contact: | Charlotte Ward |  |
| --- | --- | --- |
|  | 01277 252835 |  |
|  | cward19@ford.com |  |