1. Release version and download file name

The newly released program version and download file name is as follows.

[Release version]

<C754/C654 MFP firmware>

| Model | Program Name | Current Ver. | New Ver. | Program File Name | Note |
| --- | --- | --- | --- | --- | --- |
| bizhub C754/C654 | MFP firmware | G20-70 | GD1-70 | A2X00Y0-F000-GD1-70.exe |  |

* Please install this firmware into MFP only when you use Web Browser Function (LK-101 v3).

[Download File Name]

A2X00Y0-F000-GD1-70.exe

C754_Series_PRI_DLBT1306148EN_0.doc

2. What changed

2.1. Release of bizhub C754/C654 (Special-Program Ver.GD1-70)

The individual files and the checksum are as follows.

| Program Name | File Name | Checksum | Note |
| --- | --- | --- | --- |
| MFP Card Version | A2X00Y0-F000-GD1-70 |  |  |
| MFP Controller BOOT Program | A2X00Y0-1E00-G00-01 | EB40 |  |
| Linux-based MFP Controller | Linux-2.6.26.8-rt16 | 6F0F |  |
| MFP Controller Kernel Program | A2XK0Y0-1C00-GC1-13 | 5945 |  |
| MFP Controller Subset | A2XK0Y0-1F00-G00-07 | AFDF |  |
| MFP Controller | A2X00Y0-0100-GD1-70 | 2A45 |  |
| MFP Controller System | A2X00Y0-1000-GD1-70 |  |  |
| MFP Controller Print Controller | A2X00Y0-3000-G00-80 |  |  |
| MFP Controller Print Controller Font | A2X00Y0-3F00-G00-19 |  |  |
| MFP Controller Print Controller Demo Page | A2X00Y0-3E00-G00-01 |  |  |
| MFP Controller MIO | A2X00Y0-5000-G00-48 |  |  |
| MFP Controller PIC | A2X00Y0-8200-GC0-42 |  |  |
| Scanner | A2X00Y0-0023-G00-0B | 7EFD |  |
| Printer | A2X00Y0-0050-GC2-25 | 5724 |  |
| FAX board controller | A22M0Y0-4000-GC6-07 | 20EF |  |
| Operation panel message data | A2X00Y0-8100-GC1-70 | 0389 |  |
| ADF (DF-702) | A3CK0Y0-0024-G00-03 | B5DC |  |
| Finisher (FS-534) | A3EP0Y0-0071-G00-13 | 969A |  |
| Finisher (FS-535) | A2Y10Y0-00N1-G00-19 | 76BB |  |
| Finisher (JS-602) | --- |  |  |
| RU | A2Y10Y0-00R1-G00-04 | 43C1 |  |
| ZU | A1090Y0-00H1-G01-11 | 7BCC |  |
| SD | A3ER0Y0-0071-G00-06 | B2E8 |  |
| COPY PROTECT | --- | 56AC |  |
| Movie Data | A2X00Y0-C000-G00-00 |  |  |
| Voice Data | A2X00Y0-F000-G00-11 |  |  |
| Dictionary Data | A2X0010-B100-G00-02 |  |  |
| Engine Parameter | A2X00Y0-0054-G00-00 |  |  |

2.2. Fixed issues

The following issues are solved in this firmware.

- When perform FAX sending by Direct Input, it is able to send to the same address. [PEBJKA12009045]

- The following symptoms occur if the custom size original is copied with 2-Sided. [PEBJTK13000175]

- The image on back side is shifted to Main Scanning.

- The black line (image of Non-Image Area) is printed.

- If the large TIFF file is sent by using Scan to SMB, memory overflow does not occur and all page is not sent. [PEBJOS13000812]

In this firmware, If the large TIFF file is sent by using Scan to SMB, memory overflow occurs.

- When using Fax Forwarding function, the I-FAX job may not be forwarded if I-FAX job is received while the MFP is in sleep mode. [PEBJTS13001119]

- "CLEANING IN PROGRESS, Please Wait" is displayed on the panel without end. [PEBJTH12003574, PEBJHK12008238]

- OOXML error report is printed when specified docx file is transmitted directry to MFP. [PEBJNG13001377]

- When MFP is connected with authentication application, the amount of credit shortage warning screen is displayed even if the credit is charged from the application after the amount of credit shortage is occurred. [RIBEU_12003397]

- The main menu buttons are only named with the first characters when installing the localization firmware with Greek and Russian language. [RIBEU_13000308, RIBEU_13000208]

- Scan to SMB fails due to the login error if the access permission of shared folder is set as local user account who is not the domain user account on the domain environment. [PEBAU_13000174]

Following Software Switch is added.

Switch No. : 17

HEX Assignment 00 : Default

HEX Assignment 10 : For this issue

- C-E301 may occur when printing a large print job from PC or BOX with tri-folding every 2 pages of a document. [PEBAU_12001012]

- If you execute Initialization (Network Setting Data) on the Service Mode when External Server Authentication is set as ON, you cannot login to MFP with External Server Authentication due to the error (Authentication Fail) even if you reset the network settings. [RIIFEC12002388]

- FA14 occurs if 317x448 size document is printed with 1200dpi by using PS Driver. [RIBUR_13000353]

- Correct the following wrong Chinese wording. [RIAOAC13000068]

- offset

- You can log in by IC card while Login error occurs. [RIDSEU13000570]

- When printing from KMPU V 1.8/ HPUX 11.x, MFP may hang up. [PEBD__13000173]

- The following message may be overlapped on the control panel. [PEBJHK12009022, PEBD__12001761, PEBJKS12008364]

- “Ready to Copy” and “Scanning...”

- When you copy with the following settings, C-E301 occurs.

- Blank Page Removal + Page Number Type(1/5,2/5...) in Page Number.

- If PIV Card is pulled out during the login process, you can log in to MFP.

- If the following procedure is operated by using firmware Ver. GC6/GD6-68 and GC7/GD7-68, the black document saved in the ID & Print Use Box can not be printed by the Black only user.

1. Log in and open the ID & Print Use Box.

2. Select “Select All”.

3. Select “Reset”.

4. Select the black document.

- When Over 7 documents saved in Use Box are selected and saving to the External Memory, “Saving document.....” keeps displaying.

- When using User Authentication, Panel lock occurs if log out on Job History of send screen while Off-Hook is used.

The countermeasure of all the problems solved on GD7-68 or earlier (NOT include GH9-68 (Customized FW)) versions are included in this firmware.

3. Functional restrictions

- If the following procedure is operated by using XPS driver, all sheets are printed out as one set though multiple sets of copies are specified on the printer driver. (This is a problem caused by the application software.)

1. Set the number of copies on the Adobe Acrobat X.

2. Open "Page Setup..." and printing the job after click "OK" button.

[Workaround]

Set the number of copies in properties of the printer driver.

- An MS-Excel file that can be printed as one page with 600dpi setting may be printed in 2 pages if the resolution is changed from 600dpi to 1200dpi. (This is a problem caused by the application software.)

The following technical information is published from Microsoft.

http://support.microsoft.com/kb/400271/ja

- If the IPP connection is selected on the Port setting of XPS Driver and the preview function is enabled, the following symptom occurs. (This is a problem caused by the OS.)

-Although the print job is correctly completed, an error job remains in the spooler. The error job will be automatically deleted afterward.

- Printing becomes impossible when XPS driver is installed by the following procedure (SMB). (This is a problem caused by the OS.)

- XPS driver is installed by SMB Browsing from Network.

- XPS driver is installed by IP Address Browsing from Network.

[Workaround]

Perform the following steps, when you install the XPS driver via SMB.

1. Open the Devices and Printers, then click [Add a printer].

2. Select the [Local printer].

3. Select the [Create a new port] and choose the [Local Port].

4. Enter "\\NetBios name\service name" for the [Port Name].

- If the "readme" is opened by the Auto Run in the CD-ROM that is comes with the MFP using IE8 or IE9 then print it by using XPS preview function, an error message is displayed and it can not be printed.

This is a problem caused by the IE9.

Please do not open a file from the link of Auto Run and Please open a file directly.

- When log into the Authentication web site from Web Browser, you can not log in if characters other than one-byte characters are used.

Only one-byte characters are supported for the Authentication web site from Web Browser.

- Some content may not be displayed in the specific web site.

Please zoom in the web site.

- The Print and Delete button which has grayed out on the User Box in PSWC can be pressed.

- The function of Google and SharePointServer does not work correctly from Web Browser.

The web site (Google and SharePointServer etc.) where contents and a function are always updated is not supported.

* Refer to the Readme.txt file which is included in each driver and application for other functional restrictions.

* Additional memory installation is required when using the following Open API function.

- Initial screen customization

4. How to install

4.1. How to install program

Use USB memory to install. For the details, see the Service Manual.

Conditions for USB memory which can be used for updating the firmware are as follows:

- Securities such as data encryption and password lock shall be released, or the security function shall be turned Off.

- Memory with 1 GB to 2 GB are recommended (One with 4 GB or more may not operate)

- Compatible with USB Version 1.0/2.0 interface

- Formatted with FAT32 type

- A USB flash memory that appears as multiple drives on a computer cannot be used.

4.2. How to check card version

[ROM version]:

You can check the ROM version in service mode, "Firmware Version”

For the details, see the Service Manual.

4.3. How to install movie data

Use USB memory to install. For the details, see the Service Manual.

4.4. How to install voice data

The following options are required to use the voice guidance function.

- EK-604/ 605 (local interface kit)

- i-Option LK-104 v3

Use USB memory to install. For the details, see the Service Manual.

4.5. How to install OCR Dictionary Data for Searchable PDF and PDF/A Font Data

Use USB memory to install. For the details, see the Service Manual.

i-Option kit is required to use these functions.

4.6. How to install Unicode Font Data and OCR Font Data

Install Font Data for LPR using LPR command from the PC.

Install Font Data for USB using USB memory.

For the details, see the Service Manual.

i-Option kit is required to use these functions

4.7. How to install Loadable Driver

- Extract the attached exe file and save “xxxxxx.tar” file to root directory of USB memory.

- Insert the USB memory to USB port of MFP.

- Call the Service Mode to the screen.

- Touch [System 2] -> [Driver Install].

- Touch [SET] and press “Start” button to start installing the data.

- Check that data is normally installed from the message that appears on the control panel.

- Turn OFF/ON the main switch.

- In the Service Mode> Billing Setting> Management Function Choice, select “Card” or “Body” in “Authentication Device2” and press “OK” button.

- Turn OFF/ON the main switch.

For the details, see the Service Manual.

5. Program that recommends applying at the same time

Please refer to the PRI for “bizhub C754/C654 Mass-Production Program Maintenance Release 1 (Ver.G20-65)(for Web Browser (LK-101v3))” for details. (DLBT1201323EN*)

6. OpenAPI supported function level

The following is OpenAPI supported function level on this firmware.

OpenAPI:

| OpenAPI Function Level | 3.7.2 |
| --- | --- |

Detail:

| Auth | 1.0/1.1/2.0/2.1/2.5/3.5/3.6/3.7 |
| --- | --- |
| Scan to Application | 2.0/2.1/2.2/3.0/3.1/3.5/3.6/3.7 |
| PullPrint | 1.0/1.1/2.0/2.1/2.5/3.5/3.6 |
| Other A | 1.0/3.5 |
| Job Management | 1.0/3.5/3.6 |
| Setup | 1.0/1.1/1.2/1.3/2.0/2.1/2.5/3.5/3.6/3.7/3.8 |
| Web Browser | Auth | 1.0/1.1/1.5/3.5/3.6/3.7 |
|  | Scan to Application | 1.0/1.1/3.5/3.6/3.7 |
|  | PullPrint | 1.0/1.1/1.5/3.5/3.6 |
|  | ScrSvr | 1.0/3.5 |
|  | Launcher | 1.0/3.5 |

* Company names and product names in this document are the registered trademarks for respective companies.

Copyright(C) 2013 KONICA MINOLTA, INC.