# TRANSPORT CANADA

# MASTER MINIMUM EQUIPMENT LIST

# CANADAIR Regional Jet

# CL-600-2B19

# CL-600-2C10

# CL-600-2D15

# CL-600-2D24

# CL-600-2E25

# CSP ABC-044

First Issued:  Sep 15/92

# Revision 20:  Nov 10/10

# table of contents

Subject	Chapter/Page

# title PAGE

# TABLE OF CONTENTS	TOC-1

# Manual Approval Page

RECORD OF Revisions	rev-1

RECORD OF TEMPORARY REVISIONS	TPR-1

# USER COMMENTS

LIST OF EFFECTIVE PAGES	LEP-1

highlights of change	hoc-1

DEFINITIONS	DEF-1

abbreviations and acronyms	abb-1

preamble	Pre-1

# EQUIPMENT LIST

Air Conditioning	21-1

Auto Flight	22-1

Communications	23-1

Electrical Power	24-1

Equipment/Furnishings	25-1

Fire Protection	26-1

Flight Controls	27-1

Fuel	28-1

Hydraulic Power	29-1

Ice and Rain Protection	30-1

Indicating/Recording Systems	31-1

Landing Gear	32-1

Lights	33-1

Navigation	34-1

Oxygen	35-1

Pneumatic	36-1

Potable Water	38-1

Central Maintenance System	45-1

Information Systems	46-1

Airborne Auxiliary Power	49-1

(cont'd)

# table of contents (cont’d)

Subject	Chapter/Page

EQUIPMENT LIST (cont’d)

Doors	52-1

Engine Fuel and Control	73-1

Ignition	74-1

Engine Controls	76-1

Engine Indicating	77-1

Exhaust	78-1

Oil	79-1

Starting	80-1

TRANSPORT CANADA


MASTER MINIMUM EQUIPMENT LIST


CANADAIR Regional Jet

CL-600-2B19
CL-600-2C10
CL-600-2D15
CL-600-2D24
CL-600-2E25


CSP ABC-044
Manual Approval

Approved:
								


	Transport Canada					Walter Istchenko  
	Airworthiness Branch				Chief, Flight Test,
	Flight Test Division (AARDC)				National Aircraft Certification
	Tower ‘C’, Place de Ville				for Minister of Transport
	330 Sparks Street
	Ottawa, Ontario
	K1A 0N8
							Date:
	Telephone (613) 952-4317					

							
							Revision 20

# RECORD OF REVISIONS

Retain this index in the front of the manual. When Revisions are received and inserted, enter the relevant information in the columns below.

| Revision # | Pages Affected | By |
| --- | --- | --- |
| Original | All |  |
| 1 | Title Page Manual Approval Page User Comments LEP-1, LEP-2 HOC-1, HOC-2 21-1, 21-2, 21-4, 21-6 22-1, 22-2 23-3, 23-4 24-1, 24-2, 24-13 25-1, 25-3, 25-4 27-1, 27-2 28-1, 28-4 to 28-14 29-2 30-2, 30-3, 30-4, 30-5, 30-6 31-2 32-1 33-4, 33-5, 33-6 34-3, 34-4, 34-6 35-1, 35-2, 35-3, 35-4 36-1, 36-2 49-1, 49-2 52-2 56-2 73-2 74-1, 74-2 76-2 77-2 78-2 79-2 80-1, 80-2 |  |
| 2 | Title Page Manual Approval Page LEP-1 HOC-1, HOC-2 27-2 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 3 | Title Page Manual Approval Page Rev-1, Rev-2 TempRev-1, TempRev-2 User Comments LEP-1, LEP-2 HOC-1, HOC-2, HOC-3, HOC-4 21-1, 21-2, 21-3, 21-4, 21-5, 21-6, 21-7, 21-8 22-1, 22-2, 22-3, 22-4 23-1, 23-2, 23-3 24-1, 24-2, 24-3 25-1, 25-2, 25-4 26-2, 26-3, 26-4, 26-5, 26-6 28-1, 28-2, 28-3, 28-4 29-1, 29-2 30-1, 30-2, 30-3, 30-4, 30-5, 30-6 32-1 33-2, 33-3, 33-5, 33-6 34-1, 34-3, 34-4, 34-5 35-1, 35-2 36-1, 36-2 49-1, 49-2 52-1, 52-2, 52-3, 52-4 74-1 |  |
| 4 | All |  |
| 5 | Title Page Manual Approval Page Rev-2 LEP-1, LEP-2 HOC-1, HOC-2 23-2 24-1 30-4, 30-5, 30-6 56-1 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 6 | Title Page Manual Approval Page Rev-3, Rev-4 LEP-1 to LEP-4 HOC-1 to HOC-4 Note-3 21-1 to 21-14 23-1 to 23-8 24-1, 24-2 25-5 26-1 to 26-8 27-1 to 27-8 28-1 to 28-12 29-1 to 29-4 30-1 to 30-10 31-1 to 31-4 32-1 to 32-8 33-1 to 33-10 34-1 to 34-12 36-1 to 36-2 |  |
| 7 | All |  |
| 8 | Title Page Manual Approval Page Rev-4 TpRv-4 to TpRv-7 LEP-1 to LEP-4 HOC-1 to HOC-4 Defn-7 Abbr-12 21-1 to 21-5, 21-8, 21-9, 21-12 23-6 24-5 to 24-10 25-1 26-2, 26-4, 26-6, 26-7 27-2 to 27-5 28-1, 28-7 30-8 31-1 to 31-4 32-4 49-2 52-2 to 52-4 74-1 79-1 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 9 | All |  |
| 10 | All |  |
| 11 | Title Page Manual Approval Page Rev-4 TpRv-9 LEP-1 to LEP-4 HOC-1 23-1, 23-2 24-2, 24-3, 24-4, 24-5, 24-6, 24-7, 24-8, 24-9, 24-10, 24-11, 24-12,24-13, 24-14 25-1 26-1, 26-5, 26-10 27-1, 27-3, 27-4, 27-8, 27-9, 27-10 28-1, 28-3, 28-4, 28-5, 28-6, 28-7, 28-8, 28-9, 28-10, 28-11, 28-12, 28-13, 28-14, 28-15, 28-16, 28-17, 28-18 29-1 30-1, 30-3, 30-4, 30-6, 30-7, 30-8, 30-9, 30-10, 30-11, 30-12 32-2, 32-3 33-1, 33-2, 33-3, 33-4, 33-5, 33-6, 33-7, 33-8, 33-9, 33-10 34-1, 34-5, 34-7, 34-8, 34-9, 34-10 35-4 38-2 52-1, 52-2, 52-3, 52-4, 52-5, 52-6 73-1 74-1 |  |
| 12 | All |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 13 | Title Page Manual Approval Page Rev-5, Rev-6 TpRv-5, TpRv-6 LEP-1 to LEP-4 HOC-1 to HOC-4 21-5, 21-8, 21-9, 21-11, 21-16, 21-17 24-5, 24-6, 24-7, 24-8, 24-9 25-4 28-4, 28-7 29-1, 29-2 30-1, 30-3, 30-4 32-1, 32-2, 32-3 33-10 36-1, 36-2, 36-4, 36-5 49-2 52-5 77-1 78-1 80-1 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 14 | Title Page Manual Approval Page Rev-6 TpRv-7 to TpRv-10 LEP-1 to LEP-4 HOC-1 to HOC-4 21-1, 21-2, 21-3, 21-4, 21-6, 21-8 to 21-30 22-3 23-3, 23-5 25-3 to 25-10 26-2 27-2 to 27-10 29-1 to 29-3 30-1, 30-3 to 30-5 31-1 32-3 to 32-6 33-2, 33-7, 33-9 to 33-12 34-5 to 34-8 35-2 36-1 to 36-10 49-1, 49-3 52-1 to 52-6 74-1 |  |
| 15 | All |  |
| 16 | All |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 17 | Title Page Manual Approval Page Rev-7, Rev-8 TpRv-9 to TpRv-10 LEP-1 to LEP-4 HOC-1 to HOC-4 Def-4 to Def-6 Abb-1 21-3, 21-5 to 21-7 23-1, 23-3, 23-4, 23-8 24-3 to 24-5, 24-13 25-1, 25-6 to 25-8 26-4 27-10 28-2 to 28-5, 28-8 to 28-12 29-3 to 29-5 30-6 to 30-8, 30-12 33-2, 33-3, 33-6 34-4 35-1 38-2 52-2 73-1, 73-2 74-1, 74-2 79-1 80-1 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 18 | Title Page Manual Approval Page Rev-8 TpRv-10, TpRv-11, TpRv-12 LEP-1 to LEP-4 HOC-1 to HOC-4 21-2, 21-4 to 21-7, 21-23 23-1, 23-5, 23-10, 23-11, 23-12 24-1 to 24-5, 24-13 25-4, 25-7, 25-10, 25-12 27-1, 27-5, 27-7 to 27-9 28-1, 28-7 to 28-16 32-4 33-3, 33-9, 33-10 34-4 49-1, 49-2 73-2 |  |

| Revision # | Pages Affected | By |
| --- | --- | --- |
| 19 | Title Page TOC-1, TOC-2 Manual Approval Page Rev-9, Rev-10 TpRv-11, TpRv-12 LEP-1 to LEP-4 HOC-1 to HOC-4 21-6, 21-18, 21-23, 21-26 22-3 23-2, 23-10 to 23-12 24-1 to 24-5, 24-13 25-3 to 25-7, 25-12 26-2 to 26-10 27-1, 27-4 to 27-6, 27-12 28-6 32-4 33-4, 33-7, 33-9, 33-16 34-3, 34-8 35-1 to 35-4 36-5 45-1, 45-2 46-1, 46-2 49-1, 49-2 52-2, 52-7 74-1, 74-2 78-1, 78-2 79-1, 72-2 |  |
| 20 | All |  |

# THIS PAGE INTENTIONALLY LEFT BLANK

# RECORD OF TEMPORARY REVISIONS

Retain this index in the front of the manual. When Temporary Revisions are issued or cancelled, enter the date you insert each revision in your manual.

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 1 | 30-1 | B. J. Wormworth Chief, Flight Test, 02 April 1993 | Introduces MMEL relief for Cowl Anti-Ice Pressure Blow-Off valve (failed open) | Superseded by Rev. 3 dated 26 July 1993. |
| 2 | 27-2 |  | Introduces MMEL relief for Flight/Ground Spoiler System Introduces MMEL relief for Spoileron System Channels | Not issued. Superseded by Rev. 4 dated 20 July 1994. |
| 3 | 34-5 | K. J. Mansfield, Chief, Flight Test, 31 March 1994 | Introduces MMEL relief for FMS. | Superseded by Rev. 4 dated 20 July 1994 |
| 4 | 24-1 |  | Revises MMEL relief for IDG as a result of AD CF-93-29 | Not issued. Superseded by Rev. 4 dated 20 July 1994. |
| 5 | 76-1 | K. J. Mansfield, Chief, Flight Test, 10 June 1994 | Introduces MMEL relief for L & R Engine Speed Control System | Superseded by Rev. 4 dated 20 July 1994. |
| 6 | 28-4 | K. J. Mansfield, Chief, Flight Test, 12 May 1995 | Introduces MMEL relief for Center Tank Fuel Panel with Drain Valve | Superseded by Rev. 7 dated 03 June 1996 |
| 7 | 34-10 | K. J. Mansfield, Chief, Flight Test, 23 June 1995 | Redefine accelerate-stop penalty for both Flaps 8 and Flaps 20 in MMEL Item 34-44-1 | Superseded by Rev. 7 dated 03 June 1996. |
| 8 | 22-3 | K. J. Mansfield, Chief, Flight Test, 23 June 1995 | Revises MMEL relief for Integrated Avionics Processor System (IAPS) (Input/Output Concentrator (IOC)) | Superseded by Rev. 7 dated 03 June 1996. |
| 9 | 34-5 34-7 | K. J. Mansfield, Chief, Flight Test, 02 November 1995 | Adds MMEL relief for Head-up Guidance System and adds proviso to GPWS Mode 6. | Superseded by Rev. 7 dated 03 June 1996 |
| 10 | 27-1 27-2 | K. J. Mansfield, Chief, Flight Test, 11 December 1995 | Deletes MMEL relief for Aileron and Elevator Flutter Dampers | Superseded by Rev. 7 dated 03 June 1996 |
| 11 | 24-3, 5,6 24-7, 8,9 26-2, 3,7 49-1, 2 | K. J. Mansfield, Chief, Flight Test, 08 December 1995 | Revises MMEL APU relief for aircraft fitted with 3B1 engines | Superseded by Rev. 7 dated 03 June 1996 |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 12 | 24-4 | K. J. Mansfield, Chief, Flight Test, 08 December 1995 | Deletes MMEL ADG Auto-deploy System relief | Superseded by TR #15 dated 26 April 1996 |
| 13 | 28-5 | K. J. Mansfield, Chief, Flight Test, 15 December 1995 | Adds left boost pump proviso requiring APU to be operating | Superseded by Rev. 7 dated 03 June 1996 |
| 14 | 49-1 | R. Walker for K. J. Mansfield, Chief, Flight Test, 05 February 1996 | Corrects intent of item 49-14-02 | Superseded by Rev. 7 dated 03 June 1996 |
| 15 | 24-4 | R. Walker for K. J. Mansfield, Chief, Flight Test 26 April 1996 | Reinstated MMEL relief for ADG Auto-Deploy System and introduces relief for TRU Cooling Fans | Superseded by Rev. 7 dated 03 June 1996 |
| 16 | 21-4 |  | Adds MMEL relief for Display Unit Cooling Low Flow Detector | Not issued. Withdrawn. |
| 17 | 21-6 | R. Walker for K. J. Mansfield, Chief, Flight Test 26 April 1996 | Adds MMEL relief for Ground Air Conditioning Connector Cover | Superseded by Rev. 7 dated 03 June 1996 |
| 18 | 27-6/7 | R. Walker for K. J. Mansfield, Chief, Flight Test 26 April 1996 | Adds MMEL relief for flight spoiler and spoileron PCUs | Superseded by Rev. 7 dated 03 June 1996 |
| 19 | 21-4 | R. Walker for K. J. Mansfield, Chief, Flight Test 09 July 1996 | Adds MMEL relief for Overboard Exhaust SOV (Avionics Cooling) inoperative | Superseded by Rev. 8 dated 08 May 1997 |
| 20 | 27-3 27-4 27-5 | R. Walker for K. J. Mansfield, Chief, Flight Test 09 July 1996 | Adds an (O) Procedure and a proviso to each sub-item of 27-62-01 re T/O configuration Warning System | Superseded by Rev. 8 dated 08 May 1997 |
| 21 | 32-7 |  | Adds MMEL relief for HSTCU BITE WOW Output Drivers (WOW # 1 and WOW # 2) | Not issued. |
| 22 | 74-1 | R. Walker for K. J. Mansfield, Chief, Flight Test 09 July 1996 | Adds an (O) Procedure and NOTE to MMEL Item 74-11-01 re Continuous Ignition | Superseded by Rev. 8 dated 08 May 1997 |
| 23 | 26-7 | R. Walker for K. J. Mansfield, Chief, Flight Test 09 July 1996 | Adds MMEL relief for redundant squibs in cargo compartment fire extinguisher | Superseded by Rev. 8 dated 08 May 1997 |
| 24 | 24-5 to 24-8 | R. Walker for K. J. Mansfield, Chief, Flight Test 17 June 1996 | Deletes Main Battery and Main Battery Charger MMEL relief for IRS equipped aircraft | Superseded by Rev 8 dated 08 May 1997 |
| 25 | 26-6 | R. Walker for K. J. Mansfield, Chief, Flight Test 24 June 1996 | Adds MMEL relief for SMOKE TOILET Caution Message | Superseded by Rev. 8 dated 08 May 1997 |
| 26 | 49-2 | L. Farrell for K. J. Mansfield, Chief, Flight Test 16 July 1996 | Adds proviso to MMEL Item 49-14-2 to apply AFM performance corrections for APU air intake door open | Superseded by Rev. 8 dated 08 May 1997 |
| 27 | 27-2 | L. Farrell for K. J. Mansfield, Chief, Flight Test 26 July 1996 | Adds (M) procedure to deactivate the inoperative potentiometer | Superseded by Rev. 8 dated 08 May 1997 |
| 28 | 77-1 | Denied by TC | Adds MMEL relief for N2 Indication | Denied by TC |
| 29 | 23-6 | R. Walker for K. J. Mansfield, Chief, Flight Test 10 September 1996 | Amends MMEL relief for RTUs | Superseded by Rev. 8 dated 08 May 1997 |
| 30 | 79-1 | L. Galvin for K. J. Mansfield, Chief, Flight Test 29 October 1996 | Adds MMEL relief for Engine Oil Detection Panel | Superseded by Rev. 8 dated 08 May 1997 |
| 31 | 30-8 | L. Galvin for K. J. Mansfield, Chief, Flight Test 29 October 1996 | Introduces MMEL relief for potable water tank heaters | Superseded by Rev. 8 dated 08 May 1997 |
| 32 | 26-4 32-4 | K. Horton for K. J. Mansfield, Chief, Flight Test 10 December 1996 | Amends MMEL relief for Main Landing Gear Bay Overheat Detection System and BTMS | Superseded by Rev. 8 dated 08 May 1997 |
| 33 | 31-2 | L. Galvin for K. J. Mansfield, Chief, Flight Test, 29 October 1996 | Amends MMEL relief for DCUs by requiring the inoperative unit be deactivated | Superseded by Rev. 8 dated 08 May 1997 |
| 34 | 28-7 | L. Galvin for K. J. Mansfield, Chief, Flight Test 29 October 1996 | Amends proviso requiring APU be operating for XFLOW/APU Fuel Pump relief | Superseded by Rev. 8 dated 08 May 1997 |
| 35 | 79-1 | R. Walker, A/Chief, Flight Test, for Minister of Transport 04 July 1997 | (M) requirement added to proviso to disconnect an inoperative Oil Low Pressure switch 79-30-2 | Superseded by Rev. 9 dated 20 March 2000 (which deletes MMEL relief) |
| 36 | 80-1 | R. Walker, A/Chief, Flight Test, for Minister of Transport 04 July 1997 | Adds relief for an inoperative Engine Starter Automatic Cutout 80-12-1 | Superseded by Rev. 9 dated 20 March 2000 (which deletes MMEL relief) |
| 37 | 26-5 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Adds an (M) to deactivate the smoke detector to prevent a false warning 26-15-1 | Superseded by Rev. 9 dated 20 March 2000 (which also adds definition of ballast) |
| 38 | 36-1 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Deletes closed condition from the proviso to allow either open or closed via blanking cap 36-12-1 | Superseded by Rev. 9 dated 20 March 2000 (which changes to harmonised wording with FAA) |
| 39 | 25-1 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Adds relief for inoperative flashlights and flashlight holders 25-13-1 | Superseded by Rev. 9 dated 20 March 2000 (which also adds definition of equivalent characteristics) |
| 40 | 56-1 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Adds relief for cracked external face ply on a windshield or cockpit side window : 56-11-1 56-12-1 | Superseded by Rev. 9 dated 20 March 2000 (which deletes MMEL relief – now in AMM) |
| 41 | 34-3 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Changes relief for HUGs from category C to D. 34-32-1 | Superseded by Rev. 9 dated 20 March 2000 (which also makes editorial changes to proviso) |
| 42 | 23-6 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Adds second note to deselect inoperative RTU to allow cross-side tuning by remaining RTU 23-81-01 | Superseded by Rev. 9 dated 20 March 2000 (which modifies relief) |
| 43 | 25-5 | L. Farrell, A/Chief, Flight Test, for Minister of Transport 14 August 1997 | Adds relief for Liner in Cargo Compartment 25-52-1 | Superseded by Rev. 9 dated 20 March 2000 (which also adds definition of ballast) |
| 44 | 26-5 / TR # 37 | B. Jupp, Chief, Flight Test, for Minister of Transport 20 October 1999 | Deletes relief temporarily for Smoke Detectors for a/c with Return Catering Option 26-15-1 | Superseded by TR # 44-1 |
| 45 | 52-3 | R. Walker, A/Chief, Flight Test, for Minister of Transport 07 April 2000 | Modifies relief for Pax Door Indication System to address new Phase IV door Design Change 52-70-1 | Superseded by TR # 45-1 |
| 44-1 | 26-5 | B. Jupp, Chief, Flight Test for Minister of Transport 02 June 2000 | Deletes relief temporarily for 26-15-1 Smoke Detectors for aircraft with Universal Baggage Bay with Return Catering Option. TR # 44-1 revises title of relief, changes MMEL page affected, and deletes reference to TR # 37 to match Rev. 9 changes | Superseded by Rev. 11 dated 23 April 2001 |
| 45-1 | 52-3 | B. Jupp, Chief, Flight Test for Minister of Transport 02 June 2000 | Modifies relief for 52-70-1 Pax Door Indication System to address new Phase IV door design change. TR # 45-1 corrects sub-item 2)’s number and deletes second word flap in both provisos g) | Superseded by Rev. 10 dated 02 February 2001 |
| 46 | 25-3 34-7 | B. Jupp, Chief, Flight Test for Minister of Transport 02 June 2000 | Corrects wording for 25-16-1 to three calendar days and adds to 34-52-1 word System in title | Superseded by Rev. 10 dated 02 February 2001 |
| 47 | 24-1 24-2 24-4 49-1 | B. Jupp, Chief, Flight Test for Minister of Transport, 29 June 2001. | Adds an additional limitation to item 24-11-01 sub-item 1) & 3), 24-22-01 sub-item 1 and 49-10-01 sub-item 1. | Superseded by Rev. 12 dated 02 August 2002 |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 48 | 28-4 28-6 28-7 28-14 28-15 28-16 28-17 | B. Jupp, Chief, Flight Test for Minister of Transport, 13 February 2002. | Deletes MMEL relief temporarily for CL 600-2C10 for item 28-13-07 Transfer Ejectors (Center Tank), item 28-13-08 Fuel Transfer SOVs (Center Tank), Item 28-13-10 XFlow Pump, item 28-41-01 EICAS Fuel Tank Quantity Readouts (Left, Right and Total), item 28-41-02 EICAS Center and Total Fuel Tank Quantity Readouts and item 28-41-03 Fuel Computer Channels. | Superseded by Rev. 12 dated 02 August 2002 |
| 49 | 32-1 32-2 | L. Galvin for Chief, Flight Test, 02 August 2002. | Adds additional limitations to item 32-30-01 Landing Gear Retraction System and item 32-44-01 Anti-Skid (System) Channels. These limitations were previously addressed in the AFM Supplement. | Superseded by Rev. 12 dated 02 August 2002 |
| 50 | 21-8 21-9 21-16 21-17 30-1 30-3 30-4 36-1 36-2 36-4 36-5 | B. Jupp, Chief, Flight Test for Minister of Transport 30 October 2002. | Introduces performance penalties to items 21-51-01 Air Conditioning Packs, 21-51-02 FCV, 21-52-01 Ram Air SOV, 30-12-01 Wing A/I Mod. SOV, 30-12-04 Wing A/I Temp. Sensor Elements, 30-12-05 Wing Cross Bleed Valve, 36-11-02 PRSOV, 36-11-03 HPV, 36-12-02 Bleed Air ISOL Valve, 36-21-06 Bleed Leak Detect. Loops. These additional limitations are to compensate engine thrust loss for a/c operations with one pack in high mode or/and single bleed feeding both wings for A/I purposes. This revision also introduces the (O) procedure in item 21-52-01 and amends the title of item 30-12-01. | Superseded by Rev. 13 dated 07 November 2002 |
| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| 51 | 33-7 | B. Jupp, Chief, Flight Test for Minister of Transport, 10 Feb 2003. | Introduces new item (33-45-01) for the Sterile Light System. | Superseded by Rev. 14 dated June 03/04. |
| 52 | 30-1 30-3 30-4 | B. Jupp, Chief, Flight Test for Minister of Transport, 09 July 2003. | Introduces new sub-items in items 30-12-01 Wing Anti-Ice Modulating and SOV, 30-12-04 Wing Anti-Ice Temperature Sensor Elements and 30-12-05 Wing Cross Bleed Valve to reflect introduction of ModSum 670T122141. | Superseded by Rev. 14 dated June 03/04. |
| 53 | 27-2 27-5 | B. Jupp, Chief, Flight Test for Minister of Transport, 03 July 2003. | Introduces new MMEL Item - 27-51-03 Skew Detection System. Revises MMEL Items 27-51-01 Flap Electronic Control Unit Channels, 27-52-01 Flap Power Drive Unit Motors, and 27-54-01 Flap Position Potentiometers to reflect the impact from the installation of the Skew Detection System. In addition, this TR combines the MMEL Items 27-51-01 Flap Electronic Control Unit Channels and 27-52-01 Flap Power Drive Unit Motors. | Superseded by Rev. 14 dated June 03/04. |
| 54 | 52-2 | B. Jupp, Chief, Flight Test for Minister of Transport, 11 Sept 2003. | Introduces new MMEL Item 52-35-01 Forward Cargo Compartment Door Protector Kit. | Superseded by Rev. 14 dated June 03/04. |
| 55 | 27-8 | B. Jupp, Chief, Flight Test for Minister of Transport, 09 July 2003. | Introduces new MMEL Item 27-65-02 Spoiler and Stabilizer Control System. | Superseded by TR 65. |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 56 | 29-1 | B. Jupp, Chief, Flight Test for Minister of Transport, 04 July 2003. | Deletes CL 600-2C10 MMEL relief temporarily for item 29-11-01 “Engine Driven Pump (EDP) (Systems 1 and 2) until an appropriate EDP deactivation kit is produced. | Superseded by TR 56 Rev.1. |
| 56 Rev1 | 29-1 | B. Jupp, Chief, Flight Test for Minister of Transport, 21 January 2004. | Re-introduces CL 600-2C10 MMEL relief for item 29-11-01 “Engine Driven Pump” / Introduces CL 600-2D24 MMEL relief for item 29-11-01 “Engine Driven Pump”. | Superseded by Rev. 14 dated June 03/04. |
| 57 | 52-1 | MMEL TRS No 04 was approved by: B. Jupp, Chief, Flight Test for Minister of Transport, 17 June 2005. | This MMEL TR 57 is based on TCCA approved TRS No 04. MMEL TRS No 04 adds item 52-11-06 “Passenger Door Support Wheel Assembly”. | Superseded by Rev. 16 dated June 30/05. |
| 58 | 33-1 33-8 33-9 33-10 34-3 | TRS No 01 Rev “B” was approved by B. Jupp, Chief, Flight Test for Minister of Transport on 09 August 2004. TRS No 02 Rev “A” was approved by B. Jupp, Chief, Flight Test for Minister of Transport on 21 September 2004. | This MMEL TR is based on TCCA approved TRS No 01 Rev. “B” and TRS No 02 Rev. “A” and also corrects typographical errors. The MMEL TRS No 01 Rev. “B” modifies item 33-21-01 “Cabin Interior Lights” and item 33-51-01 “Cabin Emergency Lights” to introduce ModSum TC601R 101452, 101462, 101470 and 101520. The MMEL TRS No 02 Rev. “A” modifies item 34-42-01 “Ground Proximity Warning System” to introduce ModSum TC601R15984. | Superseded by Rev. 15 dated May 11/05. |
| 59 | 52-1 | B. Jupp, Chief, Flight Test for Minister of Transport, 10 Sept 2003. | Introduces new item (52-11-05) for Passenger Door Handrail Quick-Release Pins. | Superseded by Rev. 14 dated June 03/04. |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 60 | 22-3 | B. Jupp, Chief, Flight Test for Minister of Transport, 07 July 2003. | Introduces new item (22-22-01) Yaw Dampers. | Superseded by Rev. 14 dated June 03/04. |
| 61 | 25-5 25-7 26-4 | MMEL TRS No 09, 10 and 11 was approved by: B. Jupp, Chief, Flight Test for Minister of Transport respectively on 01, 15 and 19 September 2005. | TR 61: Modifies item 25-22-01 “Flight Attendant Seats” to introduce a sub-item for CL 600-2B19 model, Adds item 25-42-01 “Lavatory Door Springs” for all models, and Modifies item 26-15-01 “Cargo Compartment Smoke Detectors” to introduce ModSum TC601R101264 for CL 600-2B19 model. | Superseded by Rev. 17 dated August 09/06. |
| 62 | 34-5 | B. Jupp, Chief, Flight Test for Minister of Transport, 09 July 2003. | Splits 600-2B19 and 600-2C10/600-2D24 reliefs in item 34-44-01 Radio Altimeter. | Superseded by TR 65. |
| 63 | 27-4 | B. Jupp, Chief, Flight Test for Minister of Transport, 11 December 2003. | Introduces new item 27-51-04 for the Slat Disconnect Detection System. | Superseded by Rev. 14 dated June 03/04. |
| 64 | 25-03 | B. Jupp, Chief, Flight Test for Minister of Transport, 21 January 2004. | Modifies item (25-22-01) for Flight Attendant Seats. | Superseded by Rev. 14 dated June 03/04. |
| 65 | 27-8 34-5 | B. Jupp, Chief, Flight Test for Minister of Transport, 21 January 2004. | Introduces a new sub-item to Spoiler Stabilizer Control System (27-65-02) and a modification to the Radio altimeter (34-44-01). | Superseded by Rev. 14 dated June 03/04. |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 66 | 27-6 27-7 | B. Jupp, Chief, Flight Test for Minister of Transport, 04 Dec 2003. | Deletes sub-item 3) “Spoileron Channels” in item 62-01 “Spoiler Electronic Control Unit (SECU) Channels” and deletes item 27-62-03 “Spoileron PCUs” temporarily. | Superseded by Rev. 14 dated June 03/04. |
| 67 | 29-2 | B. Jupp, Chief, Flight Test for Minister of Transport, 18 Dec 2004. | Introduces new item (29-11-08) “Hydraulic Firewall SOV” (CL 600-2C10/-2D24). | Superseded by Rev. 14 dated June 03/04. |
| 68 | 21-4 21-6 27-7 27-8 27-9 32-4 | MMEL TRS No 16 was approved by: B. Jupp, Chief, Flight Test for Minister of Transport, 06 February 2007. MMEL TRS No 18 was approved by: B. Jupp, Chief, Flight Test for Minister of Transport, 18 January 2007. | Adds in items 21-31-01 Automatic CPCs and 21-32-01 Outflow Valves limitation for takeoffs and landings on runways that may lead to imminent ditching. Introduces a new item 32-45-01 Parking Brake Handle Locking Positions (Clockwise and Counter-clockwise) for all models. Modifies items 27-62-01 “Spoiler Electronic Control Unit (SECU) Channels” and 27-62-03 “Spoileron PCUs” to introduce SECU p/n 49-164-07 and 49-164-21 for CL-600-2B19 model. Modifies the second limitation of item 27-62-03 “Spoileron PCUs” so that one operative spoileron PCU per spoileron surface is controlled by a SECU p/n 49-164-05, 49-164-07 or 49-164-21 (for CL-600-2B19 model). | Superseded by Rev. 18 dated October 30/07. |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 69 | 28-11 | TRS No. 22 B. Jupp, Chief, Flight Test for Minister of Transport, 13 April 2007. | Item 28-40-01 EICAS Bulk Fuel Temperature Indication made applicable to CL-600-2D15 and CL-600-2D24 models. | Superseded by Rev. 18 dated October 30/07. |
| 70 | 52-7 | TRS No. 26 B. Jupp, Chief, Flight Test for Minister of Transport, 11 December 2007. | The reliefs for the FWD and CTR Door Indication Systems, item 52-70-04, are deleted. | Superseded by Rev. 19 dated July 23/09. |
| 71 | 24-2 27-11 | TRS No. 24, 27 Dick Walker, Acting Chief, Flight Test for Minister of Transport, 24 November 2008. | In the item 29-11-01 Integrated Drive Generators (IDG), the engine operating hour changes to flight hour for sub-items 1) and 2) Constant Speed Drives; Items 27-51-02 Slat/Flap System is modified to address new ModSum 670T31194 | Superseded by Rev. 19 dated July 23/09. |
| 72 | 23-10 23-11 | TRS No. 30 Jim Martin, for Acting Chief, Flight Test for Minister of Transport, 27 March 2009. | Item 23-82-01 COM/NAV Standby Tuning Unit is modified to address new ModSums 670T122173 or 670T31608 (elimination of the standby radio tuning unit); Items 23-81-01 RTU #2 and 23-82-02 FMS TUNE INHIBIT Switch are modified to address new ModSums 670T122173 or 670T31608 and reconsider dispatch conditions for redundant tuning units. | Superseded by Rev. 19 dated July 23/09. |

| Temp Rev # | Pages Affected | TC approval | Description of Revision | Date Incorporated Signature |
| --- | --- | --- | --- | --- |
| 73 | 27-4 27-5 | TRS No. 31 Dick Walker, Acting Chief, Flight Test for Minister of Transport, 24 April 2009. | MMEL TRS No 31 modifies two items; 27-51-02 Slat / Flap System and 27-51-05 Flap System to split each of them into two sub-items as result of introduction of new Modsum 670T31732, and a new sub-item for aircraft with Modsum 670T31732 is introduced with no maintenance procedure. | Superseded by Rev. 19 dated July 23/09. |
| 74 | 34-6 | TRS No. 33 James J. Manton, Acting Chief, Flight Test for Minister of Transport, 13 October 2009. | MMEL TRS No 33 modifies item 34-50-01 to expand and cover the differences between IRS operation in NAV mode and ATT mode, and the Operational Procedures are added to Navigation Function relief. | Superseded by Rev. 20 dated November 10/10. |
| 75 | 28-11 | TRS No. 32 Walter Istchenko, Acting Chief, Flight Test for Minister of Transport, 16 December 2009. | MMEL TRS No 32 modifies item 28-40-01 to introduce new dispatch conditions for the Bulk Fuel Temperature indication failure, and the Maintenance Procedure is removed from relief conditions. | Superseded by Rev. 20 dated November 10/10. |
| 76 | 52-7 | TRS No. 34 Walter Istchenko, Chief, Flight Test for Minister of Transport, 13 April 2010. | MMEL TRS No 34 modifies item 52-70-04 Cargo Compartment Door Indication System; sub-items 1) FWD and 2) CTR are reintroduced for aircraft with modsum 670T31862 installed. | Superseded by Rev. 20 dated November 10/10. |
| 77 | 30-5 | TRS No. 29 Walter Istchenko, Chief, Flight Test for Minister of Transport, 21 April 2010. | MMEL TRS No 29 introduces the new item 30-12-08 Outboard Low Heat Switches for the model 600-2B19 with the ModSum TC601R17364 TC601R17494. | Superseded by Rev. 20 dated November 10/10. |
| 78 | 21-8 | TRS No. 35 Walter Istchenko, Chief, Flight Test for Minister of Transport, 14 May 2010. | MMEL TRS No 35 introduces the new ModSums 670T82406 (production) and 670T040476 (in-service) for the item 21-40-01 Galley Heating System, CL-600-2C10/-2D15/-2D24 models. | Superseded by Rev. 20 dated November 10/10. |

November 10/10

# CL-600-2B19 / CL-600-2C10 / CL-600-2D15 / CL-600-2D24 / CL-600-2E25 Canadair Regional Jet

# MMEL USER COMMENTS

# ON ERRORS, OMISSIONS, PROCEDURES (IF APPLICABLE), ETC.

# FAX to:		(514) 855-7970

Bombardier Aerospace

MMEL Section Chief

# OR

# Email to:	jean-pierre.dargis@aero.bombardier.com

# OR

# Mail to:		address on back of this page

# From:							Telephone No.:

Company:						Email address:

Date:

# The MMEL requires the following correction or clarification:

ATA Chapter / MMEL Item No.:

Page No.:						Page Date:

# OUR RESPONSE

# Thank you for your comment;

( We will issue Temporary Revision No.____

( We will include in Revision ___ scheduled for:

Comment:

Date:

--------------------------------------------------------------------------------------------------------------------------------------------------------

# Bombardier Aerospace

P.O.Box 6087, Station Centre-ville

Montreal, Quebec

H3C 3G9

# Attention:	MMEL Section Chief

Dept. 066

--------------------------------------------------------------------------------------------------------------------------------------------------------

# LIST OF EFFECTIVE PAGES

| CHAPTER PAGE DATE | CHAPTER PAGE DATE |
| --- | --- |
| Title Page November 10/10 Table of Contents TOC-1 November 10/10 TOC-2 November 10/10 Manual November 10/10 Approval Page Record of Revisions Rev-1 June 30/05 Rev-2 June 30/05 Rev-3 June 30/05 Rev-4 June 30/05 Rev-5 June 30/05 Rev-6 June 30/05 Rev-7 August 09/06 Rev-8 October 30/07 Rev-9 November 10/10 Rev-10 November 10/10 Record of Temporary Revisions TpRv-1 June 30/05 TpRv-3 June 30/05 TpRv-4 June 30/05 TpRv-5 June 30/05 TpRv-6 June 30/05 TpRv-7 June 30/05 TpRv-8 June 30/05 TpRv-9 August 09/06 TpRv-10 October 30/07 TpRv-11 July 23/09 TpRv-12 November 10/10 TpRv-13 November 10/10 User November 10/10 Comments List of Effective Pages LEP-1 November 10/10 LEP-2 November 10/10 LEP-3 November 10/10 LEP-4 November 10/10 | Highlights Of Change HOC-1 November 10/10 HOC-2 November 10/10 HOC-3 November 10/10 HOC-4 November 10/10 HOC-5 November 10/10 HOC-6 November 10/10 HOC-7 November 10/10 HOC-8 November 10/10 HOC-9 November 10/10 HOC-10 November 10/10 HOC-11 November 10/10 HOC-12 November 10/10 HOC-13 November 10/10 Definitions Def-1 November 10/10 Def-2 November 10/10 Def-3 November 10/10 Def-4 November 10/10 Def-5 November 10/10 Def-6 November 10/10 Abbreviations and Acronyms Abb-1 November 10/10 Abb-2 November 10/10 Abb-3 November 10/10 Abb-4 November 10/10 Abb-5 November 10/10 Abb-6 November 10/10 Abb-7 November 10/10 Abb-8 November 10/10 Abb-9 November 10/10 Abb-10 November 10/10 Abb-11 November 10/10 Abb-12 November 10/10 Preamble Pre-1 November 10/10 Pre-2 November 10/10 21 Air Conditioning 21-1 November 10/10 21-2 November 10/10 21-3 November 10/10 |

# LIST OF EFFECTIVE PAGES (cont’d)

| CHAPTER PAGE DATE | CHAPTER PAGE DATE |
| --- | --- |
| 21-4 November 10/10 21-5 November 10/10 21-6 November 10/10 21-7 November 10/10 21-8 November 10/10 21-9 November 10/10 21-10 November 10/10 21-11 November 10/10 21-12 November 10/10 21-13 November 10/10 21-14 November 10/10 21-15 November 10/10 21-16 November 10/10 21-17 November 10/10 21-18 November 10/10 21-19 November 10/10 21-20 November 10/10 21-21 November 10/10 21-22 November 10/10 21-23 November 10/10 21-24 November 10/10 21-25 November 10/10 21-26 November 10/10 21-27 November 10/10 21-28 November 10/10 22 Auto Flight 22-1 November 10/10 22-2 November 10/10 22-3 November 10/10 22-4 November 10/10 23 Communications 23-1 November 10/10 23-2 November 10/10 23-3 November 10/10 23-4 November 10/10 23-5 November 10/10 23-6 November 10/10 23-7 November 10/10 23-8 November 10/10 23-9 November 10/10 23-10 November 10/10 23-11 November 10/10 23-12 November 10/10 | 24 Electrical Power 24-1 November 10/10 24-2 November 10/10 24-3 November 10/10 24-4 November 10/10 24-5 November 10/10 24-6 November 10/10 24-7 November 10/10 24-8 November 10/10 24-9 November 10/10 24-10 November 10/10 24-11 November 10/10 24-12 November 10/10 24-13 November 10/10 24-14 November 10/10 25 Equipment/Furnishings 25-1 November 10/10 25-2 November 10/10 25-3 November 10/10 25-4 November 10/10 25-5 November 10/10 25-6 November 10/10 25-7 November 10/10 25-8 November 10/10 25-9 November 10/10 25-10 November 10/10 25-11 November 10/10 25-12 November 10/10 25-13 November 10/10 25-14 November 10/10 25-15 November 10/10 25-16 November 10/10 26 Fire Protection 26-1 November 10/10 26-2 November 10/10 26-3 November 10/10 26-4 November 10/10 26-5 November 10/10 26-6 November 10/10 26-7 November 10/10 26-8 November 10/10 26-9 November 10/10 26-10 November 10/10 |

# LIST OF EFFECTIVE PAGES (cont’d)

| CHAPTER PAGE DATE | CHAPTER PAGE DATE |
| --- | --- |
| 27 Flight Controls 27-1 November 10/10 27-2 November 10/10 27-3 November 10/10 27-4 November 10/10 27-5 November 10/10 27-6 November 10/10 27-7 November 10/10 27-8 November 10/10 27-9 November 10/10 27-10 November 10/10 27-11 November 10/10 27-12 November 10/10 28 Fuel 28-1 November 10/10 28-2 November 10/10 28-3 November 10/10 28-4 November 10/10 28-5 November 10/10 28-6 November 10/10 28-7 November 10/10 28-8 November 10/10 28-9 November 10/10 28-10 November 10/10 28-11 November 10/10 28-12 November 10/10 28-13 November 10/10 28-14 November 10/10 28-15 November 10/10 28-16 November 10/10 29 Hydraulic Power 29-1 November 10/10 29-2 November 10/10 29-3 November 10/10 29-4 November 10/10 29-5 November 10/10 29-6 November 10/10 | 30 Ice & Rain Protection 30-1 November 10/10 30-2 November 10/10 30-5 November 10/10 30-6 November 10/10 30-7 November 10/10 30-8 November 10/10 30-9 November 10/10 30-10 November 10/10 30-11 November 10/10 30-12 November 10/10 31 Instruments 31-1 November 10/10 31-2 November 10/10 31-3 November 10/10 31-4 November 10/10 Landing Gear 32-1 November 10/10 32-2 November 10/10 32-3 November 10/10 32-4 November 10/10 32-5 November 10/10 32-6 November 10/10 33 Lights 33-1 November 10/10 33-2 November 10/10 33-3 November 10/10 33-4 November 10/10 33-5 November 10/10 33-6 November 10/10 33-7 November 10/10 33-8 November 10/10 33-9 November 10/10 33-10 November 10/10 33-11 November 10/10 33-12 November 10/10 33-13 November 10/10 33-14 November 10/10 33-15 November 10/10 33-16 November 10/10 33-17 November 10/10 33-18 November 10/10 |

# LIST OF EFFECTIVE PAGES (cont’d)

| CHAPTER PAGE DATE | CHAPTER PAGE DATE |
| --- | --- |
| 34 Navigation 34-1 November 10/10 34-2 November 10/10 34-3 November 10/10 34-4 November 10/10 34-5 November 10/10 34-6 November 10/10 34-7 November 10/10 34-8 November 10/10 35 Oxygen 35-1 November 10/10 35-2 November 10/10 35-3 November 10/10 35-4 November 10/10 36 Pneumatics 36-1 November 10/10 36-2 November 10/10 36-3 November 10/10 36-4 November 10/10 36-5 November 10/10 36-6 November 10/10 36-7 November 10/10 36-8 November 10/10 36-9 November 10/10 36-10 November 10/10 38 Water/Waste 38-1 November 10/10 38-2 November 10/10 45 Central Maintenance Systems 45-1 November 10/10 45-2 November 10/10 46 Information Systems 46-1 November 10/10 46-2 November 10/10 49 Airborne Auxiliary Power 49-1 November 10/10 49-2 November 10/10 49-3 November 10/10 49-4 November 10/10 49-5 November 10/10 49-6 November 10/10 | 52 Doors 52-1 November 10/10 52-2 November 10/10 52-3 November 10/10 52-4 November 10/10 52-5 November 10/10 52-6 November 10/10 52-7 November 10/10 52-8 November 10/10 73 Engine Fuel and Control 73-1 November 10/10 73-2 November 10/10 74 Ignition 74-1 November 10/10 74-2 November 10/10 76 Engine Control 76-1 November 10/10 76-2 November 10/10 77 Engine Indicating 77-1 November 10/10 77-2 November 10/10 78 Exhaust 78-1 November 10/10 78-2 November 10/10 79 Oil 79-1 November 10/10 79-2 November 10/10 80 Starting 80-1 November 10/10 80-2 November 10/10 |

# HIGHLIGHTS OF CHANGE

Revision 20 introduces the model CL-600-2E25.

The Temporary Revisions No 74, No 75, No 76, No 77 and No 78 are superseded by the Rev. 20.

# SUMMARY OF TECHNICAL AND EDITORIAL CHANGES

| Item No | Type of change | Summary of changes |
| --- | --- | --- |
| 21-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-23-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-23-02 | Technical | The model 600-2E25 is introduced in this item. |
| 21-24-02 | Technical | The model 600-2E25 is introduced in this item. |
| 21-24-03 | Technical | The model 600-2E25 is introduced in this item. |
| 21-24-07 | Technical | The model 600-2E25 is introduced in this item. |
| 21-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-31-02 | Technical | The model 600-2E25 is introduced in this item. |
| 21-31-03 | Technical | The model 600-2E25 is introduced in this item. |
| 21-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-33-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-40-01 | Technical | The new ModSums 670T82406 (production) and 670T040476 (in-service) are introduced for the CL-600-2C10/-2D15/-2D24 models. The model 600-2E25 is introduced in this item. |
| 21-50-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-51-03 | Technical | The model 600-2E25 is introduced in this item. |
| 21-51-04 | Technical | The model 600-2E25 is introduced in this item. |
| 21-52-02 | Technical | The model 600-2E25 is introduced in this item. |
| 21-52-03 | Technical | The item is reintroduced for 600-2C10, -2D15, -2D24 models. |

| Item No | Type of change | Summary of changes |
| --- | --- | --- |
| 21-55-03 | Technical | The model 600-2E25 is introduced in this item. |
| 21-55-04 | Technical | The model 600-2E25 is introduced in this item. |
| 21-55-05 | Technical | The model 600-2E25 is introduced in this item. |
| 21-61-01 | Technical | The model 600-2E25 is introduced in this item. |
| 21-61-04 | Technical | The model 600-2E25 is introduced in this item. |
| 22-10-01 | Technical | The model 600-2E25 is introduced in this item. |
| 22-10-02 | Technical | The model 600-2E25 is introduced in this item. The note for T/O CONFIG OK is addressed in the relief. |
| 22-11-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 22-11-02 | Technical | The model 600-2E25 is introduced in this item. |
| 22-11-03 | Technical | The model 600-2E25 is introduced in this item. |
| 22-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 22-12-02 | Technical | The model 600-2E25 is introduced in this item. |
| 22-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 22-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-22-02 | Technical | The model 600-2E25 is introduced in this item. |
| 23-22-03 | Technical | The model 600-2E25 is introduced in this item. |
| 23-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-31-02 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 23-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-40-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 23-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 23-51-03 | Technical | The model 600-2E25 is introduced in this item. |
| 23-51-04 | Technical | The model 600-2E25 is introduced in this item. |
| 23-51-05 | Technical | The model 600-2E25 is introduced in this item. |
| 23-51-06 | Technical | The model 600-2E25 is introduced in this item. |
| 23-71-01 | Technical | The model 600-2E25 is introduced in this item. |
| 23-81-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-11-02 | Technical | The model 600-2E25 is introduced in this item. |
| 24-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-23-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-24-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-31-02 | Technical | The model 600-2E25 is introduced in this item. |
| 24-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-32-02 | Technical | The model 600-2E25 is introduced in this item. |
| 24-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-41-02 | Technical | The model 600-2E25 is introduced in this item. |
| 24-41-03 | Technical | The model 600-2E25 is introduced in this item. |
| 24-50-03 | Technical | The model 600-2E25 is introduced in this item. |
| 24-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 24-61-02 | Technical | The model 600-2E25 is introduced in this item. |
| 25-00-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-12-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 25-18-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-18-02 | Technical | The model 600-2E25 is introduced in this item. |
| 25-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-23-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 25-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-40-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-40-02 | Technical | The model 600-2E25 is introduced in this item. |
| 25-40-03 | Technical | The model 600-2E25 is introduced in this item. |
| 25-42-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 25-51-03 | Technical | The model 600-2E25 is introduced in this item. |
| 25-51-04 | Technical | The model 600-2E25 is introduced in this item. |
| 25-52-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-61-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-61-02 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 25-61-03 | Technical | The model 600-2E25 is introduced in this item. |
| 25-61-04 | Technical | The model 600-2E25 is introduced in this item. |
| 25-62-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-64-01 | Technical | The model 600-2E25 is introduced in this item. |
| 25-70-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 26-00-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-00-02 | Technical | The model 600-2E25 is introduced in this item. |
| 26-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-14-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-15-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-16-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 26-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-23-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-25-01 | Technical | The model 600-2E25 is introduced in this item. |
| 26-25-02 | Technical | The model 600-2E25 is introduced in this item. |
| 26-26-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 27-00-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-15-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-15-02 | Technical | The model 600-2E25 is introduced in this item. |
| 27-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-24-02 | Technical | The model 600-2E25 is introduced in this item. |
| 27-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-35-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 27-51-04 | Technical | The Mod Sum 670T30446 is introduced for models 600-2C10/2D15/2D24 |
| 27-51-05 | Technical | The model 600-2E25 is introduced in this item. |
| 27-60-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-65-01 | Technical | The model 600-2E25 is introduced in this item. |
| 27-65-02 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-01 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-02 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-03 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-04 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-07 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-08 | Technical | The model 600-2E25 is introduced in this item. |
| 28-13-10 | Technical | The model 600-2E25 is introduced in this item. |
| 28-23-01 | Technical | The model 600-2E25 is introduced in this item. |
| 28-23-02 | Technical | The model 600-2E25 is introduced in this item. |
| 28-24-03 | Technical | The model 600-2E25 is introduced in this item. |
| 28-24-04 | Technical | The model 600-2E25 is introduced in this item. |
| 28-25-01 | Technical | The model 600-2E25 is introduced in this item. |
| 28-25-02 | Technical | The model 600-2E25 is introduced in this item. |
| 28-25-03 | Technical | The model 600-2E25 is introduced in this item. |
| 28-25-04 | Technical | The model 600-2E25 is introduced in this item. |
| 28-25-05 | Technical | The model 600-2E25 is introduced in this item. |
| 28-40-01 | Technical | Item is modified to introduce new dispatch conditions for the Bulk Fuel Temperature indication failure, and the Maintenance Procedure is removed from relief conditions The model 600-2E25 is introduced in this item. |
| 28-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 28-41-02 | Technical | The model 600-2E25 is introduced in this item. |
| 28-41-03 | Technical | The model 600-2E25 is introduced in this item. |
| 28-41-04 | Technical | The model 600-2E25 is introduced in this item. |
| 28-41-05 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-03 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-04 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-05 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-06 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-07 | Technical | The model 600-2E25 is introduced in this item. |
| 29-11-08 | Technical | The model 600-2E25 is introduced in this item. |
| 29-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 29-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 29-34-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-12-04 | Technical | The model 600-2E25 is introduced in this item. |
| 30-12-05 | Technical | The model 600-2E25 is introduced in this item. |
| 30-12-06 | Technical | The model 600-2E25 is introduced in this item. |
| 30-12-08 | Technical | The new item Outboard Low Heat Switches is introduced for the model 600-2B19 with the ModSum TC601R17364 TC601R17494. |
| 30-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-22-03 | Technical | The model 600-2E25 is introduced in this item. |
| 30-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-31-02 | Technical | The model 600-2E25 is introduced in this item. |
| 30-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-42-01 | Technical | The model 600-2E25 is introduced in this item. |
| 30-71-02 | Technical | The model 600-2E25 is introduced in this item. |
| 30-81-01 | Technical | The model 600-2E25 is introduced in this item. |
| 31-14-01 | Technical | The model 600-2E25 is introduced in this item. |
| 31-14-02 | Technical | The model 600-2E25 is introduced in this item. |
| 31-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 31-31-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 31-31-02 | Technical | The model 600-2E25 is introduced in this item. |
| 31-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 31-41-02 | Technical | The model 600-2E25 is introduced in this item. |
| 31-41-03 | Technical | The model 600-2E25 is introduced in this item. |
| 31-41-04 | Technical | The model 600-2E25 is introduced in this item. |
| 31-41-05 | Technical | The model 600-2E25 is introduced in this item. |
| 31-61-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-30-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-40-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-43-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-44-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-45-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-46-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-46-02 | Technical | The model 600-2E25 is introduced in this item. |
| 32-47-01 | Technical | The model 600-2E25 is introduced in this item. |
| 32-50-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-13-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-21-02 | Technical | The model 600-2E25 is introduced in this item. |
| 33-23-02 | Technical | The model 600-2E25 is introduced in this item. |
| 33-24-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-41-02 | Technical | The model 600-2E25 is introduced in this item. |
| 33-42-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-43-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-44-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-44-02 | Technical | The model 600-2E25 is introduced in this item. |
| 33-45-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-46-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 33-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 34-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-14-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-22-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-25-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-32-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-41-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-41-02 | Technical | The model 600-2E25 is introduced in this item. |
| 34-42-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-42-02 | Technical | The model 600-2E25 is introduced in this item. |
| 34-42-03 | Technical | The model 600-2E25 is introduced in this item. |
| 34-43-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 34-44-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-44-02 | Technical | The model 600-2E25 is introduced in this item. |
| 34-45-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-50-01 | Technical | Item is modified to expand and cover the differences between IRS operation in NAV mode and ATT mode, and the Operational Procedures are added to Navigation Function relief. The model 600-2E25 is introduced in this item. |
| 34-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 34-52-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-53-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-54-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-61-01 | Technical | The model 600-2E25 is introduced in this item. |
| 34-61-02 | Technical | The model 600-2E25 is introduced in this item. |
| 35-10-01 | Technical | The model 600-2E25 is introduced in this item. |
| 35-10-02 | Technical | The model 600-2E25 is introduced in this item. |
| 35-11-02 | Technical | The model 600-2E25 is introduced in this item. |
| 35-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 35-12-02 | Technical | The model 600-2E25 is introduced in this item. |
| 35-20-01 | Technical | The model 600-2E25 is introduced in this item. |
| 35-20-02 | Technical | The model 600-2E25 is introduced in this item. |
| 35-20-03 | Technical | The model 600-2E25 is introduced in this item. |
| 35-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 35-31-02 | Technical | The model 600-2E25 is introduced in this item. |
| 36-11-04 | Technical | The model 600-2E25 is introduced in this item. |
| 36-21-06 | Technical | The model 600-2E25 is introduced in this item. |
| 38-10-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 38-30-01 | Technical | The model 600-2E25 is introduced in this item. Item is modified to bring In line with the TCCA Guidance Book. |
| 38-30-02 | Technical | The model 600-2E25 is introduced in this item. |
| 45-45-01 | Technical | The model 600-2E25 is introduced in this item. |
| 45-45-02 | Technical | The model 600-2E25 is introduced in this item. |
| 46-20-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-10-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-14-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-43-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-51-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-51-02 | Technical | The model 600-2E25 is introduced in this item. |
| 49-61-01 | Technical | The model 600-2E25 is introduced in this item. |
| 49-61-02 | Technical | The model 600-2E25 is introduced in this item. |
| 52-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 52-11-05 | Technical | The model 600-2E25 is introduced in this item. |
| 52-11-06 | Technical | The model 600-2E25 is introduced in this item. |
| 52-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 52-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 52-35-01 | Technical | The model 600-2E25 is introduced in this item. |
| 52-70-01 | Technical | The model 600-2E25 is introduced in this item. |
| 52-70-02 | Technical | The model 600-2E25 is introduced in this item. |
| 52-70-03 | Technical | The model 600-2E25 is introduced in this item. |
| 52-70-04 | Technical | Item is modified to reintroduce the sub-items 1) FWD and 2) CTR for aircraft with modsum 670T31862 installed. The model 600-2E25 is introduced in this item. |
| 52-70-05 | Technical | The model 600-2E25 is introduced in this item. |
| 73-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 73-31-04 | Technical | The model 600-2E25 is introduced in this item. |
| 74-11-01 | Technical | The model 600-2E25 is introduced in this item. |
| 74-30-02 | Technical | The model 600-2E25 is introduced in this item. |
| 76-10-02 | Technical | The model 600-2E25 is introduced in this item. |
| 76-11-03 | Technical | The model 600-2E25 is introduced in this item. |
| 77-31-01 | Technical | The model 600-2E25 is introduced in this item. |
| 78-30-01 | Technical | The model 600-2E25 is introduced in this item. |
| 79-12-01 | Technical | The model 600-2E25 is introduced in this item. |
| 79-21-01 | Technical | The model 600-2E25 is introduced in this item. |
| 79-30-01 | Technical | The model 600-2E25 is introduced in this item. |
| 79-30-03 | Technical | The model 600-2E25 is introduced in this item. |
| 80-10-01 | Technical | The model 600-2E25 is introduced in this item. |
| 80-10-02 | Technical | The model 600-2E25 is introduced in this item. |
| 80-11-03 | Technical | The model 600-2E25 is introduced in this item. |

# Please retain these sheets until the next revision has been issued.

# DEFINITIONS

# Column 1

- “System & Sequence Numbers” are based on Air Transport Association (ATA) Specification No. 100 and items are numbered sequentially.

- “Item” means the equipment, system, component, or function listed in the “Item” column.

- Repair Intervals: All users of an MEL must effect repairs of inoperative systems or components, deferred in accordance with the MEL at or prior to the repair times established by the following letter designators:

Category “A”: Items in this category shall be repaired within the time interval specified in the remarks column of the operator’s approved MEL, excluding the day the malfunction was recorded in the Aircraft Maintenance Record/Logbook.

Category “B”: Items in this category shall be repaired within three (3) consecutive calendar days (72 hours), excluding the day the malfunction was recorded in the Aircraft Maintenance Record/Logbook. For example, if it were recorded at 10 a.m. on January 26th, the three-day interval would begin at midnight the 26th and end at midnight the 29th.

Category “C”: Items in this category shall be repaired within ten (10) consecutive calendar days (240 hours), excluding the day the malfunction was recorded in the Aircraft Maintenance Record/Logbook. For example, if it were recorded at 10 a.m. on January 26th, the 10-day interval would end at midnight February 5th.

Category “D”: Items in this category shall be repaired within one hundred and twenty (120) consecutive calendar days (2880 hours), excluding the day the malfunction was recorded in the Aircraft Maintenance Record/Logbook.

The letter designators are inserted adjacent to Column 2.

- “***” symbol indicates an item which is not required by Regulations but which may have been installed on some models of aircraft covered by this MMEL. This item may be included on the operator’s MEL after the approving office has determined that the item has been installed on one or more of the operator’s aircraft. The symbol, however, shall not be carried forward into the operator’s MEL. It should be noted that neither this policy nor the use of this symbol provide authority to install or remove an item from an aircraft. The “***” symbol may be considered equivalent to the term “if installed”.

# Column 2

- “Number Installed” is the number (quantity) of items installed in the aircraft. This number represents the aircraft configuration considered in developing this MMEL. Should the number be a variable (e.g., passenger cabin items) a number is not required.

- “-“ symbol indicates a variable number (quantity) of the item installed.

NOTE:	Where the MMEL shows a variable number installed, the MEL must reflect the actual number installed or an alternate means of configuration control approved by Transport Canada.

# Column 3

- “Number Required For Dispatch” is the minimum number (quantity) of items required for operation provided the conditions specified in Column 4 are met.

- “-“ symbol indicates a variable number (quantity) of the item required for dispatch.

NOTE:	Where the MMEL shows a variable number required for dispatch, the MEL must reflect the actual number required for dispatch or an alternate means of configuration control approved by Transport Canada.

# Column 4

- “Remarks or Exceptions” in this column includes a statement either prohibiting or permitting operation with a specific number of items inoperative, provisos (conditions and limitations) for such operation, and appropriate notes.

- “(M)” symbol indicates a requirement for a specific maintenance procedure which must be accomplished prior to operation with the listed item inoperative. Normally these procedures are accomplished by maintenance personnel; however, other personnel may be qualified and authorized to perform certain functions. Procedures requiring specialized knowledge or skill, or requiring the use of tools or test equipment should be accomplished by maintenance personnel. The satisfactory accomplishment of all maintenance procedures, regardless of who performs them, is the responsibility of the operator.

Appropriate procedures, including the identification of qualified personnel authorized to accomplish them are required to be published as part of the operator’s manual or MEL.

- “(O)” symbol indicates a requirement for a specific operations procedure which must be accomplished in planning for and/or operating with the listed item inoperative. Normally these procedures are accomplished by the flight crew; however, other personnel may be qualified and authorized to perform certain functions. The satisfactory accomplishment of all procedures, regardless of who performs them, is the responsibility of the operator.

Appropriate procedures are required to be published as part of the operator’s manual or MEL.

These procedures are outlined in the Dispatch Deviation Guide, CSP A-091 (600-2B19),
CSP-BC-091 (600-2C10/-2D15/-2D24). If a procedure is not covered in the Dispatch Deviation Guide, the procedural requirements can be found in the provisos of the MMEL or in the relevant Airplane Flight Manual (AFM).

NOTE:	The (M) and (O) symbols are required in the operator’s MEL unless otherwise authorized by Transport Canada.

- Alphabetical symbol indicates a proviso (condition or limitation) that must be complied with for operation with the listed item inoperative.

- NOTES provide additional information for crewmember or maintenance consideration. Notes are used to identify applicable material which is intended to assist with compliance, but do not relieve the operator of the responsibility for compliance with all applicable requirements. Notes are not a part of the provisos.

- Deleted in the remarks column after a sequence item indicates that the item was previously listed but is now required to be operative if installed in the aircraft.

# ADDITIONAL DEFINITIONS

- “Administrative Control Item” means an item listed by the operator in the MEL for tracking and information purposes. It may be added to an operator’s MEL provided no relief is granted, or provided conditions and limitations are contained in an approved document (i.e., Structural Repair Manual, Airworthiness Directive, etc.). If relief other than that granted by an approved document is sought for an administrative control item, a request must be submitted to Transport Canada. If the request results in review and approval, the item becomes an MMEL item rather than an administrative control item.

- “Airplane Flight Manual” (AFM) is the document required for type approval and approved by Transport Canada. The approved AFM for the specific aircraft is listed on the applicable Type Approval Data Sheet.

- “As required by Regulations” and other similar statements mean that the listed item is subject to certain provisions (restrictive or permissive) expressed in the Federal Aviation Regulations (FARs), Airworthiness Manual (AWM) or Canadian Aviation Regulations (CARs). The number of items specified by these requirements must be operative. When the listed item is not required by the requirements, it may be inoperative for the time specified by repair category.

- “Change bar”: A vertical bar in the margin indicates a change, addition or deletion in the adjacent text for the current revision of that page only. The change bar is dropped at the next revision of that page.

- Day of Discovery is the calendar day an equipment/instrument malfunction was recorded in the Aircraft Maintenance Logbook and/or Record. This day is excluded from the calendar days or flight days specified in the MMEL for the repair of an inoperative item of equipment, and is applicable to all MMEL items in categories A,B,C, and D.

- “Deactivated” and “Secured” means that the specified component must be put into an acceptable condition for safe flight. An acceptable method of securing or deactivating will be established by the operator.

- Engine Indicating Crew Alerting System (EICAS) that provides electronic messages refers to a system capable of providing different priority levels of system information messages (e.g., WARNING, CAUTION, ADVISORY and STATUS).  Any airplane discrepancy message that affects dispatchability will be at the WARNING, CAUTION or STATUS level.

- “ER” refers to extended range operations of a two-engine airplane which has a type design approval for ER operations and complies with the provisions of TP 6327 (ETOPS).

- “Excess Items” means those items that have been installed but are redundant to the requirements.

- “Extended Overwater Operations” means operations over water at a horizontal distance of more than 50 nautical miles from the nearest shoreline.

- .”Federal Aviation Regulations” (FARs) means the applicable portions of the Federal Aviation Act and Federal Aviation Regulations.

- “Flight Day” means a 24-hour period (from midnight to midnight) either Universal Coordinated Time (UCT) or local time, as established by the operator, during which at least one flight is initiated for the affected aircraft.

- “Icing Conditions” means an atmospheric environment that may cause ice to form on the aircraft or in the engine(s).

- “Inoperative” means a system and/or a component malfunction to the extent that it does not accomplish its intended purpose and/or is not consistently functioning normally within its approved operating limit(s) or tolerance(s).

- Inoperative components of an inoperative system: Inoperative items which are components of a system which is inoperative are usually considered components directly associated with and having no other function than to support that system. (Warning/caution systems associated with the inoperative system must be operative unless relief is specifically authorized per the MMEL).

- “Passenger Convenience Items” means those items related to passenger convenience, comfort or entertainment such as, but not limited to, galley equipment, movie equipment, ash trays, stereo equipment, overhead reading lamps, etc.

- Placarding: Each inoperative item must be placarded to inform and remind the crewmembers and maintenance personnel of the equipment condition.

NOTE:	To the extent practical, placards should be located adjacent to the control or indicator for the item affected; however, unless otherwise specified, placard wording and location will be determined by the operator.

- “Visual Flight Rules” (VFR) is as defined in the CARs. This precludes a pilot from filing an Instrument Flight Rules (IFR) flight plan.

- “Visual Meteorological Conditions” (VMC) means the atmospheric environment is such that would allow a flight to proceed under the visual flight rules applicable to the flight. This does not preclude operating under Instrument Flight Rules.

- “Visible Moisture” means an atmospheric environment containing water in any form that can be seen in natural or artificial light; for example, clouds, fog, rain, sleet, hail, or snow.

- “Considered Inoperative” means that item must be treated for dispatch, taxi and flight purposes as though it were inoperative.  The item shall not be used or operated until the original deferred item is repaired.  Additional actions include: documenting the item on the dispatch release (if applicable), placarding, and complying with all remarks, exceptions, and related MMEL provisions, including any (M) and (O) procedures and observing the repair category.

- “Is not used” in the provisos, remarks or exceptions for an MMEL item may specify that another item relieved in the MMEL “is not used.”   In such cases, crewmembers should not activate, actuate, or otherwise utilize that component or system under normal operations.  It is not necessary for the operators to accomplish the (M) procedures associated with the item.  However, operational requirements must be complied with, and an additional placard must be affixed, to the extent practical, adjacent to the control or indicator for the item that is not used to inform crewmembers that a component or system is not to be used under normal operations.

# THIS PAGE INTENTIONALLY LEFT BLANK

# abbreviations and acronyms

The following abbreviations and acronyms may be used on flight compartment displays, radio tuning units and the flight management system or may be found in this manual. Some abbreviations may appear in upper or lower case letters. Abbreviations which have limited usage are explained in the chapters where they are used.

| A |  |
| --- | --- |
| a/c, A/c Aircraft | AHC Attitude Heading |
| A/C Air Conditioning A/G Air/Ground A/ICE Anti-ice A/P Autopilot A/S Airspeed A/SKID Anti-skid ABS Absolute AC Alternating Current ACARS ARINC Communications Addressing and reporting System ACCEL Acceleration, accelerate(d), accelerometers ACM Air Cycle Machine ACMP Alternating Current Motor Pump/ Electric Hydraulic Pump ACT Active ACU Air Conditioning Unit ADC Air Data Computer ADDR Address ADF Automatic Direction Finder ADG Air Driven Generator ADI Attitude Director Indicator ADS Air Data System AFCS Automatic Flight Control System AFT Afterward AGL Above Ground Level | Computer AHRS Attitude Heading Reference System AIL Aileron ALIGN Aligning, alignment ALPHA alpha ALT Altitude, Altimeter ALT Altitude Hold (PFD/FD) ALT CAP Altitude Capture (PFD/FD) ALT HOLD Altitude Hold ALTN Alternate ALTS Selected Altitude Arm/Abort (PFD/FD) AM Amplitude Modulation AMB Ambient AMP Amperes ANNUN Annunciator ANT Antenna AOA Angle of Attack AP Autopilot APC Auxiliary Power Control APP Approach APPROX Approximately APR Automatic Performance Reserve APU Auxiliary Power Unit ARINC Aeronautical Radio Incorporated ARP Air Data Reference Panel |

| ASYM Asymmetrical ATA Air Transport Association ATC Air Traffic Control ATT Attitude ATTD Attitude ATTND Attendant AUTO Automatic | AUTO BAL Automatic Balance AUTO XFER Automatic Transfer AUX Auxiliary AV Avionics AVAIL Available AZ Azimuth |
| --- | --- |

| B |  |
| --- | --- |
| B/AIR Bleed Air B/C Back Course B/CRS Back Course B/LEAK Bleed Leak BARO Barometric BAT Battery BATT Battery BDI Bearing Distance Indicator BFO Beat Frequency Oscillator BITE Built-In-Test Equipment | BK Brake BLD Bleed BOOM Headset microphone BRG Bearing BRKR(s) Breaker(s) BRT Bright BTL Bottle BTMS Brake Temperature Monitoring System BTMU Brake Temperature Monitoring Unit BYPS Bypass |

| C |  |
| --- | --- |
| C Center, Caution, Cabin CAA Civil Aviation Authority (UK) CAL Calibrate CAP Capture CAPT Captain CAS Calibrated Air Speed CARs Canadian Aviation Regulations CAT Category CAT II Category II CB, C/B Circuit Breaker CBP Circuit Breaker Panel | CCW Counter Clockwise CDL Configuration Deviation List CDP Compressor Discharge Pressure CDU Control Display Unit CFM Cubic Feet Per Minute CG Center of Gravity CH Chapter, Channel CHAN Channel CHGR Charger CHR Chronograph CHRT Chart |

| CK Check CKPT Cockpit CKT Circuit CLB Climb CLK Clock cm Centimeters CMD Command CMPS Compass CMPTR Computer CO2 Carbon Dioxide COM Communication COMM Communication COMP Compressor, Comparator COMPT Compartment COND Condition, Continued CONFIG Configuration | CONN Connection CONT Control, Continuous, Contactor, Controller COOL Cooling CORR Correction CPAM Cabin Pressure Acquisition Module CPLT Copilot CRS Course CRT Cathode Ray Tube CRZ Cruise CSD Constant Speed Drive CTR Center CVR Cockpit Voice Recorder CW Clockwise CYL Cylinder |
| --- | --- |

| D |  |
| --- | --- |
| DA Drift Angle DBU Data Base Unit DC Direct Current DCP Display Control Panel DCU Data Concentrator Unit DDG Dispatch Deviation Guide DECEL Decelerate(d) DECR Decrease DEFL Defuel DEG Degree DEPR Depressurize DEPT Departure DEST Destination DET Detector DEV Deviation DFDAU Digital Flight Data Acquisition Unit | DFDR Digital Flight Data Recorder DG Directional Gyro DH Decision Height DIFF Differential DIM Dimming DIR Direct DIS Distance (to way point), Disconnect DISC Disconnect DISCH Discharge DISP Dispatch, Display DIST Distance DME Distance Measuring Equipment DN Down DOT Department of Transport (Canada) DR Door |

| E |  |
| --- | --- |
| EAS Equivalent Airspeed ECAM Electronic Centralized Aircraft Monitoring System ECP EICAS Control Panel ECS Environmental Control System ECU Electronic Control Unit ED EICAS Display EDP Engine Driven Pump/ Engine Primary Hydraulic Pump EFIS Electronic Flight Instrument System EGT Exhaust Gas Temperature EICAS Engine Indication and Crew Alerting System EL Elevation | ELEC Electrical ELEV Elevator, Elevation ELT Emergency Locator Transmitter EMER(G) Emergency ENG Engine EPC External Power Contactor EQUIP Equipment ERP Eye Reference Position Datum ESS Essential ET Elapsed Time ETA Estimated Time of Arrival EVAC Evacuation EXH Exhaust EXTIN Extinguish(ed) |

| F |  |
| --- | --- |
| F/CTL Flight Controls FAA Federal Aviation Administration (USA) FAIL Failure FCC Flight Control Computer FCU Fuel Control Unit FD, F/D Flight Director FDAU Flight Data Acquisition Unit FDR Flight Data Recorder (Digital) FECU Flaps Electronic Control Unit FEED Feeder FF, F/F Fuel Flow | FIRE BTL Fire Bottle FIREX Fire Extinguisher FL CH Flight Level Change FLD Field FLT Flight FLT DIR Flight Director FLUOR Fluorescent FM Fan Marker FMS Flight Management System FPM Feet Per Minute FREQ Frequency ft Feet, Foot FW Fire Wall FWD Forward |

| G |  |
| --- | --- |
| G (+/-) Receiver Gain G/S Glide slope GA Go-around GAL Gallon GALY Galley GCS Ground Clutter Suppression GCU Generator Control Unit GE General Electric GEN Generator | GLD Ground Lift Dumping GMT Greenwich Mean Time GND Ground GPM Gallons Per Minute GPWS Ground Proximity Warning System GR Gear GRAV Gravity GS Ground Speed GUIDE Guidance GW Gross Weight |

| H |  |
| --- | --- |
| HDG Heading HDG HOLD Heading Hold HDG SEL Heading Select HEAT Heater HF High Frequency (3 – 30 m Hz) Hg Mercury HI High HLDR Holder HOR, HORIZ Horizontal HOT High Oil Temperature HP High Pressure | HPA Hecto Pascals I Horizontal Situation Indicator HSTA Horizontal Stabilizer Trim HSTCU Horizontal Stabilizer Trim Control Unit HTR Heater HUD Heads-up Display HYD Hydraulic Hz Hertz |

| I |  |
| --- | --- |
| IB, I/B, INBD Inboard I/C Intercom, Inspection Check IAPS Integrated Avionics Processor System IAS Indicated Air Speed ICAO International Civil Aviation Organization ICS Idle Corrected Speed | ID Identification IDENT Identification IDG Integrated Drive Generator IFR Instrument Flight Rules IGN Ignition |

| IB,I/B,INBD Inboard I/C Intercom, Inspection Check IAPS Integrated Avionics Processor System IAS Indicated Air Speed ICAO International Civil Aviation Organization ICS Idle Corrected Speed ILS Instrument Landing System IM ILS Inner Marker IMC Instrument Meteorological Conditions IMP. Imperial in. Inch, Inches in. Hg Inches of Mercury INCR Increase IND Indication, Indicator INFLT In Flight | INHIB Inhibit INOP Inoperative INPH Interphone INSP Inspection INST(S) Instrument(s) INST, INSTR Instrument INT Internal, Integral, Intersection INTEG Integral IRS Inertial Reference System IRU Inertial Reference Unit ISA International Standard Atmosphere ISO International Standard Organization ISOL Isolation, Isolated ITT Inter Turbine Temperature |
| --- | --- |

| J |  |
| --- | --- |
| JAA Joint Aviation Authorities |  |

| K |  |
| --- | --- |
| K, KT, KTS Knots kg Kilogram(s) kHz Kilohertz | KIAS Knots Indicated Airspeed kW(s) Kilowatt(s) |

| L |  |
| --- | --- |
| L Left, Landing L/T Landing/Taxi LAV Lavatory lb Pound(s) | LCN Load Classification Number LCV Load Control Valve LDG Landing LDG GR Landing Gear |

| LDU Lamp Driver Unit LE Leading Edge LG Landing Gear LGC Landing Gear Controller LGW Landing Gross Weight LH Left Hand LIM Limit LK Leak LN Left Nose LNAV Lateral Navigation LOC ILS Localizer LOGO Logo Graphic | LOM, MM Compass Locator at Outer Marker LOP Low Oil Pressure LP Low Pressure LPM Liter Per Minute LR Left Rear LRC Long Range Cruise LRU Line Replaceable Unit LSB Lower Side Band LT(s) Light(s) LW Left Wing LWD Left Wing Down LWR Lower |
| --- | --- |

| M |  |
| --- | --- |
| M Mach Number m Meter MAA Maximum Authorized IFR Altitude MAC Mean Aerodynamic Chord MAG Magnetic MAINT Maintenance MALF Malfunction MAB Manual MAP Ground Map (WXR) MAX Maximum MAZ MLS Azimuth MB Millibars MCA Minimum Crossing Altitude MCT Maximum Continuous Thrust MDA Minimum Descent Altitude MEA Minimum Enroute IFR Altitude MECH Mechanic MED Medium | MEL Minimum Equipment List MFD Multifunction Display MGP MLS Glideslope MHz Megahertz MI Miles MIC Microphone MID AFT Middle Afterward MID FWD Middle Forward MILS .001 of an inch MIN Minimum MISC Miscellaneous MKR Marker MLG Main Landing Gear MLI Magnetic Level Indicator MLS Microwave Landing System MLW Maximum Landing Weight MM ILS Middle Marker MMEL Master Minimum Equipment List |

| MMO Maximum Operating Speed in Mach Number MOCA Minimum Obstruction Clearance Altitude MOD Module MON Monitor MPH Miles Per Hour MRA Minimum Reception Altitude | MSG Message MSL Mean Sea Level MTBF Mean Time Before Failure MTG Miles to Go MTOW Maximum Takeoff Weight MTW Maximum Taxi Weight MZFW Maximum Zero Fuel Weight |
| --- | --- |

| Misc |  |
| --- | --- |
| % Percent & and | °C Degrees Centigrade °F Degrees Fahrenheit |

| N |  |
| --- | --- |
| N/A Not applicable N1 Low Pressure Rotor N2 High Pressure Rotor NAV Navigation ND Nose Down, Navigation Display NDB (ADF) Nondirectional Beacon (Automatic Direction Finder) NEG Negative NEUT Neutral | NL Nose Left NLG Nose Landing Gear NM Nautical Mile(s) No. Number NOPT No Procedure Turn Required NORM Normal NOSE Nosewheel NR Nose Right NU Nose Up |

| O |  |
| --- | --- |
| OAT Outside Air Temperature OB/OUTBD Outboard OBS Observer OEI One Engine Inoperative | OEW Operating Empty Weight OH, OVHD Overhead OK Okay OM ILS Outer Marker OVBD Overboard |

| OVHT, OH Overheat OVLD Overload OVSP Overspeed | OVSPD Overspeed OVTEMP Over Temperature OXY, O2 Oxygen |
| --- | --- |

| P |  |
| --- | --- |
| P#6 Panel 6 P/S Pitot/Static PA Passenger Address PASS Passenger PBE Portable Breathing Equipment (Smoke Hood) PCU Power Control Unit PF Pilot Flying PFD Primary Flight Display PLA Power Lever Angle PLT(s) Pilot(s) PNF Pilot Not Flying PNLS(s) Panel(s) PO Outside Air Pressure POS Position PPH Pounds Per Hour PRESS Pressure, Pressurization | PRI Primary PRIM Primary PROC Procedure PROT Protection PROX Proximity PSEU Proximity Sensor Electronics Unit PSI Pounds Per Square Inch PSIG Pounds Per Square Inch Gauge PSS Proximity Sensor System PSU Passenger Service Unit PT2 Engine Inlet Pressure PTCT Protect PTT Push To Talk PWR Power |

| Q |  |
| --- | --- |
| QAR Quick Access Recorder QEC Quick Engine Change QFE Local Station Pressure | QNH Altimeter Setting QTY Quantity |

| R |  |
| --- | --- |
| R Right RA Radio Altitude Resolution Advisory RAT Ram Air Turbine | RCCB Remote Controlled Circuit Breaker RCDR Recorder RCVR Receiver |

| RDR Radar REC Receiver, Recorder RECOG Recognition REF(s) Reference(s) REFL Refuel REV Reverse RH Right Hand RMI Radio Magnetic Indicator ROT Rotation RPM Revolutions Per Minute | RT, R/T Receiver-Transmitter RTE DATA Route Data RTO Rejected Takeoff RTU Radio Tuning Unit RUD Rudder RVR Runway Visual Range RVSM Reduced Vertical Separation Mininum RVSR Reverser RW Right Wing RWD Right Wing Down RWY Runway |
| --- | --- |

| S |  |
| --- | --- |
| S Status SAT Static Air Temperature SCAV Scavenge SEC Second, Secondary SECS Spoiler Electronic Control System SECU Spoiler Electronic Control Unit SEL Select, Selector SEL CAL Selective Call SENS Sensitivity, Sensor SERV, SVCE Service SMKG Smoking SOV Shutoff Valve | SP, SPD Speed SPKR Speaker SPLR(s) Spoiler(s) SQL Squelch SSB Single Side Band STA Station STAB Stabilizer STAT Status STBY Standby STEER Steering SUPPL Supply SW(s) Switches SYN Synchronize SYNC Synchronous SYS, SYST System |

| T |  |
| --- | --- |
| TA Traffic Alert T/C Top of Climb T/D Top of Descent T/R Thrust Reverser TACAN UHF Tactical Air Navigation Aid TAS True Airspeed | TAT Total Air Temperature TCAS Traffic Alert and Collision Avoidance System TE Trailing Edge TEMP Temperature TGT Target |

| TO, T/O Takeoff TOL Tolerance TRB, TURB Turbulence TRK Track TRM Trim | TRU Transformer Rectifier Unit TT2 Engine Inlet Temperature |
| --- | --- |

| U |  |
| --- | --- |
| UNSCHD Unscheduled USB Upper Side Band | USG United States Gallons UTIL Utility |

| V |  |
| --- | --- |
| V Volt VA Design Maneuvering Speed VB Design Speed for Maximum Gust Intensity VC Design Cruising Speed VD Design Diving Speed VDF/MDF Demonstrated flight diving speed. VF Design Flap Speed VDF/MFC Maximum Speed for Stability Characteristics VFE Maximum Flap Extended Speed VH Maximum Speed in Level Flight with Maximum Continuous Power VLE Maximum Landing Gear Extended Speed VLO Maximum Landing Gear Operating Speed VLOF Lift-off Speed VMC Minimum Control Speed with the Critical Engine Inoperative | VMO/MMO Maximum Operating Limit Speed VMU Minimum Unstick Speed VNE Never-exceed Speed VNO Maximum Structural Cruising Speed VR Rotation Speed VS Stalling Speed or the Minimum Steady Flight Speed at which the Airplane is Controllable VS0 Stalling Speed or the Minimum Steady Flight Speed in the Landing Configuration VS1 Stalling Speed or the Minimum Steady Flight Speed Obtained in a Specific Configuration VX Speed for Best Angle of Climb VY Speed for Best Rate of Climb Safety Speed |

| V1 Takeoff Decision Speed (formerly Denoted as Critical Engine Failure Speed) V2 Takeoff Safety Speed V2 Minimum Takeoff Safety Speed V/S Vertical Speed VERT Vertical VFR Visual Flight Rules VG Vertical Gyro VHF Very High Frequency (30 – 300 m Hz) | VIB Vibration VMC Visual Meteorological Conditions VNAV Vertical Navigation VOL Volume VOLT Voltage VOR VHF Omni directional Range Station VORTAC VOR and TACAN Co-located VSI Vertical Speed Indicator |
| --- | --- |

| W |  |
| --- | --- |
| W Warning W/C Wind Component W/S Wind Shear W/W Wheel Well WARN Warning WF Runway Length Limited Weight WGT Weight WHLS Wheels | WIND Window WOW Weight-On-Wheels WPT(s) Waypoint(s) WRN Warning WS Second Segment Limited Weight WSHLD Windshield WX Weather WXR Weather Radar |

| X |  |
| --- | --- |
| X Cross Transfer XFER, XFR Transfer XFLOW Cross Flow XMIT Transmit | XPNDR Transponder XTK Cross Track XWC Cross Wind Component |

| Y |  |
| --- | --- |
| YD, Y/D Yaw Damper |  |

| Z |  |
| --- | --- |
| ZFW Zero Fuel Weight |  |

# preamble

All equipment installed on an aircraft in compliance with the Airworthiness Standards and Operating Rules must be operative. However, Canadian Aviation Regulations (605.07, 704.07 and 705.07) permit the publication of a Minimum Equipment List (MEL) where compliance with certain equipment requirements is not necessary in the interests of safety under all operating conditions. Experience has shown that with the various levels of redundancy designed into aircraft, operation of every system or installed component may not be necessary when the remaining operative component can provide the required level of safety.

A Master Minimum Equipment List (MMEL) is developed by Transport Canada, with participation by the aviation industry, to improve aircraft utilization and thereby provide more convenient and economic air transportation for the public. The approved MMEL includes those items of equipment related to airworthiness and operating regulations and other items of equipment Transport Canada finds may be inoperative and yet maintain the required level of safety by appropriate conditions and limitations; it does not contain obviously required items such as wings, flaps, and rudders.

The MMEL is the basis for development of individual operator MELs which take into consideration the operator’s particular aircraft equipment configuration and operational conditions. Operator MELs, for administrative control, may include items not contained in the MMEL; however, relief for administrative control items must be approved. An operator’s MEL may differ in format from the MMEL, but cannot be less restrictive than the MMEL. The individual operator’s MEL, when approved and authorized, permits operation of the aircraft with inoperative equipment.

Equipment not required by the operation being conducted and equipment in excess of the requirements are included in the MEL with appropriate conditions and limitations. The MEL must not deviate from the Aircraft Flight Manual Limitations, Emergency Procedures or with Airworthiness Directives. It is important to remember that all equipment related to the airworthiness and the operating regulations of the aircraft not listed on the MMEL must be operative.

Suitable conditions and limitations in the form of placards, maintenance procedures, crew operating procedures and other restrictions as necessary are specified in the MEL to ensure that the required level of safety is maintained.

The MEL is intended to permit operation with inoperative items of equipment for a period of time until repairs can be accomplished. It is important that repairs be accomplished at the earliest opportunity. In order to maintain the required level of safety and reliability, the MMEL establishes limitations on the duration of and conditions for operation with inoperative equipment. The MEL provides for release of the aircraft for flight with inoperative equipment. When an item of equipment is discovered to be inoperative, it is reported by making an entry in the Aircraft Maintenance Record/Logbook. The item is then either repaired or may be deferred per the MEL or other approved means acceptable to Transport Canada prior to further operation. MEL conditions and limitations do not relieve the operator from determining that the aircraft is in condition for safe operation with items of equipment inoperative.

Operators are responsible for exercising the necessary operational control to ensure that the required level of safety is maintained. When operating with multiple inoperative items, the interrelationships between those items and the effect on aircraft Operation and crew workload must be considered.

Operators are to establish a controlled and sound repair program including the parts, personnel, facilities, procedures, and schedules to ensure timely repair.

WHEN USING THE MEL, COMPLIANCE WITH THE STATED INTENT OF THE PREAMBLE, DEFINITIONS, AND THE CONDITIONS AND LIMITATIONS SPECIFIED IN THE MEL IS REQUIRED.

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 22-01 | Recirculation Fans |  |  |  |  |  |
|  | 1) 600-2C10 | C | 2 | 0 | (M) May be inoperative provided affected fan(s) is deactivated. |  |
|  | 2) 600-2D15, 600-2D24 | C | 2 | 0 | (M) May be inoperative provided: Affected fan(s) is deactivated, Inlet Cargo Air SOV is operative or secured CLOSED, AIR CONDITIONING Cargo switch is selected to OFF, and Live animals are not carried in cargo compartment. |  |
|  | 3) 600-2E25 | C | 2 | 0 | (M) May be inoperative provided: Affected fan is deactivated, and Both Air Conditioning Packs are operative. | ¦ ¦ ¦ |
| 23-01 | FWD Exhaust Fan |  |  |  |  |  |
|  | Galley (600-2B19) | C | 1 | 0 | (M) May be inoperative provided: Fan is deactivated, and AFT Exhaust Fan is considered inoperative. |  |
|  | 2) Galley (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative provided fan is deactivated. | ¦ |
|  | 3) Galley/ Lavatory *** (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative provided fan is deactivated. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-2 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 23-02 | AFT Exhaust Fan (Lavatory) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M) May be inoperative provided: Fan is deactivated, and FWD Exhaust Fan is considered inoperative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (M) May be inoperative provided fan is deactivated. | ¦ |
| 24-01 | ARINC Supply Fans (Avionics Cooling) (600-2B19) | C | 2 | 1 | (M) One may be inoperative provided: Exhaust Fan (Avionics Cooling) is verified operative, and One Air Conditioning Pack is verified operative. NOTE: Utilization of equipment in the avionics bay without air conditioning and fans should be avoided during ground operation. |  |
| 24-02 | Display Cooling Fans |  |  |  |  |  |
|  | 1) 600-2B19 | C | 3 | 2 | (M) One may be inoperative provided remaining Display Cooling Fans are verified operative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 2 | 1 | (M)(O) One may be inoperative provided display check valve is verified operative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-3 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-03 | Exhaust Fan (Avionics Cooling) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M) May be inoperative provided: Both ARINC Supply Fans are verified operative, Two Display Unit Supply Fans are verified operative, and Both Air Conditioning Packs are verified operative. NOTE: Utilization of equipment in the avionics bay without air conditioning and fans should be avoided during ground operation. |  |
|  | 2) 600-2C10 with ModSum 670T10548 (Dual Fan), 600-2D15, 600-2D24 | C | 2 | 1 | (M) May be inoperative provided one Air Conditioning Pack is operative. |  |
|  | 3) 600-2E25 | C | 2 | 1 | (M) May be inoperative provided both Air Conditioning Packs are operative. | ¦¦ |
| 24-04 | Display Units Cooling Air SOV (600-2B19) | C | 1 | 0 | (M) May be inoperative provided SOV is deactivated and secured OPEN. |  |
| 24-05 | Inboard Exhaust SOV (600-2B19) | C | 1 | 0 | (M) May be inoperative provided SOV is deactivated and secured OPEN. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-06 | Overboard Exhaust SOV (Avionics Cooling) (600-2B19) | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: SOV is secured OPEN, Operations are conducted unpressurized at or below 10000 ft. MSL, and Extended overwater operations are prohibited. |  |
|  | 1) With S.B. 601R-52-001 (Enlarged vent flap) | C | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Inboard exhaust SOV is secured OPEN, Both Air Conditioning Packs are operative, Service door locking mechanism is verified operative, Service door is CLOSED, LATCHED and LOCKED, and Passenger Door and Service Door Indication Systems are operative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-07 | Ground Valve (Avionics Cooling) (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative CLOSED. | ¦ |
| 31-01 | Automatic Cabin Pressurization Controllers |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | One may be inoperative provided Cabin Pressure Acquisition Module (CPAM) of Cabin Pressure Monitoring Sub-system is operative. |  |
|  |  | C | 2 | 0 | (O) May be inoperative provided: Cabin Pressure Acquisition Module (CPAM) of Cabin Pressure Monitoring Sub-system is operative, Operations are conducted unpressurized at or below 10,000 ft MSL, and Takeoffs and landings are not conducted on runways that may lead to imminent ditching. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 2 | 1 | (O) One may be inoperative provided: Manual control system is verified operative, and Cabin Pressure Controller Panel (CPCP) Pressure Monitoring Function of Cabin Pressure Monitoring Sub-system is operative. | ¦ |
|  |  | C | 2 | 0 | (O) Both may be inoperative provided: Cabin Pressure Controller Panel (CPCP) Pressure Monitoring Function of Cabin Pressure Monitoring Sub-system is operative, Operations are conducted unpressurized at or below 10,000 ft MSL, Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and Takeoffs and landings are not conducted on runways that may lead to imminent ditching. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-02 | EMER DEPRESS Switch Guard |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | May be missing provided: Both Air Conditioning Packs are operative, and Operations are conducted at or below FL 250. |  |
|  |  | C | 1 | 0 | (O) May be missing provided operations are conducted unpressurized at or below 10,000 ft MSL. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | May be missing provided operations are conducted at or below 15,000 ft MSL. |  |
|  |  | C | 1 | 0 | (O) May be missing provided: Operations are conducted unpressurized at or below 10,000 ft MSL, and Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable). |  |
|  | 3) 600-2E25 | C | 1 | 0 |  | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-03 | Cabin Pressure Control Manual Mode (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided Outflow Valve is considered inoperative. | ¦ |
|  | MAN ALT Switch | C | 1 | 0 | (O) May be inoperative provided: Pressure control is not selected to MAN, EMER DEPRESS switch is selected ON, Operations are conducted unpressurized at or below 10,000 feet MSL, Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and Extended overwater operations are prohibited. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-8 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-01 | Outflow Valves |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 0 | (M)(O) May be inoperative provided: Affected valve(s) is secured OPEN, Overboard Exhaust SOV (Avionics Cooling) is secured OPEN, Operations are conducted unpressurized at or below 10,000 ft MSL, Extended overwater operations are prohibited, and Takeoffs and landings are not conducted on runways that may lead to imminent ditching. |  |
|  | 2) 600-2C10 | C | 1 | 0 | (M)(O) May be inoperative provided: Affected valve is secured OPEN, Operations are conducted unpressurized at or below 10,000 ft MSL, and Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable). |  |
|  | 3) 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (M)(O) May be inoperative provided: Affected valve is secured OPEN, Floatation Valve is checked for integrity, Operations are conducted unpressurized at or below 10,000 ft MSL, and Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable). | ¦ |
| 32-02 | Floatation Valve (600-2C10 with ModSum MM670T11933) | D | 1 | 0 | (M) May be inoperative provided valve is removed. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-9 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 33-01 | Cabin Pressure Monitoring Sub-system |  |  |  |  |  |
|  | 1) Cabin Pressure Acquisition Module (CPAM) (600-2B19) | C | 1 | 0 | (M) May be inoperative provided: Both Automatic Cabin Pressurization Controllers are operative, and Operations are conducted at or below FL 300. |  |
|  | 2) Cabin Pressure Control Panel (CPCP) Pressure Monitoring Function (600-2C10, 600-2D15, 600-2D24, 600-2E25) | A | 1 | 0 | (O) May be inoperative as indicated by “CPAM FAIL” status message provided: Both Automatic Cabin Pressure Controllers are operative, Emergency depress system is verified operative, Operations are conducted at or below FL 300, and Repairs are made within one flight day. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-10 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | Galley Heating System (600-2B19 with SB 601R-25-012 or SB 601R-25-033, and SB 601R-25-034), (600-2C10, 600-2D15, 600-2D24 without ASB 670BA-21-011, or 600-2C10, 600-2D15, 600-2D24 with ASB 670BA-21-011, and SB 670BA-21-013), or (600-2C10, 600-2D15, 600-2D24 with Modsum 670T82406 or 670T040476), (600-2E25) | C | 1 | 0 | (M) May be inoperative provided the system is deactivated. | ¦ |
|  | 1) Fan (600-2B19) | C | 1 | 0 | May be inoperative provided: Galley heating fan switch is selected OFF, and Galley heating #1 switch is selected OFF. |  |
|  | 2) Heater #1 (600-2B19) | C | 1 | 0 | May be inoperative provided galley heating #1 switch is selected OFF. |  |
|  | 3) Heater #2 (600-2B19) | C | 1 | 0 | May be inoperative provided galley heating #2 switch is selected OFF. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-11 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 50-01 | Ground Air Conditioning Connector Cover *** | B | 1 | 0 | (M) May be inoperative or missing provided: Connector check valve is verified CLOSED, Operations are conducted at or below FL 250, and Extended overwater operations are prohibited. |  |
| 51-01 | Air Conditioning Packs |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | (O) RH pack may be inoperative provided: RH pack is selected OFF, Operations are conducted at or below FL 250, and Ram Air SOV is verified operative. |  |
|  |  | C | 2 | 1 | (O) LH pack may be inoperative provided: LH pack is selected OFF, Operations are conducted at or below FL 250, and Ram Air SOV is either verified operative or deactivated OPEN. |  |
|  |  | C | 2 | 0 | (M)(O) Both may be inoperative provided: Both packs are selected OFF, Operations are conducted unpressurized at or below 10000 ft. MSL, Ram Air SOV is either verified operative or deactivated OPEN, EMER DEPRESS switch is selected ON, Overboard Exhaust SOV (Avionics Cooling) is secured OPEN, and Extended overwater operations are prohibited. NOTE: Ground operations should be limited at ambient temperatures greater than 30 degrees Celsius, to prolong service life of avionics components. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-12 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Air Conditioning Packs (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10 | C | 2 | 1 | (O) RH pack may be inoperative provided: RH pack is selected OFF, Operations are conducted at or below FL 310, Ram Air SOV is either verified operative or deactivated OPEN, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 1 | (O) LH pack may be inoperative provided: LH pack is selected OFF, Operations are conducted at or below FL 310, Ram Air SOV is verified operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 0 | (O) Both may be inoperative provided: Both packs are selected OFF, Ram Air SOV is either verified operative or deactivated OPEN, Operations are conducted unpressurized at or below 10000 ft. MSL, Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and Extended overwater operations are prohibited. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-13 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Air Conditioning Packs (cont’d) |  |  |  |  |  |
|  | 3) 600-2D15, 600-2D24 | C | 2 | 1 | (O) RH pack may be inoperative provided: RH pack is selected OFF, Operations are conducted at or below FL 250, Ram Air SOV is either verified operative or deactivated OPEN, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 1 | (O) LH pack may be inoperative provided: LH pack is selected OFF, Operations are conducted at or below FL 250, Ram Air SOV is verified operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 0 | (O) Both may be inoperative provided: Both packs are selected OFF, Ram Air SOV is either verified operative or deactivated OPEN, Inlet Cargo Air SOV is operative or secured CLOSED, AIR CONDITIONING Cargo switch is selected to OFF, Live animals are not carried in cargo compartment, Operations are conducted unpressurized at or below 10000 ft. MSL, Procedures are established and used to ensure the cargo compartment remains empty, or are verified to contain only empty cargo handling equipment, ballast (ballast may be loaded in ULDs), and/or Fly Away Kits, and Extended overwater operations are prohibited. NOTE: Operator MELs must define which items are approved for inclusion in the Fly Away Kits, and which materials can be used as ballast. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-14 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Air Conditioning Packs (cont’d) |  |  |  |  |  |
|  | 4) 600-2E25 | C | 2 | 2 | Must be operative for dispatch | ¦ |
| 51-02 | Flow Control Valve (FCV) |  |  |  |  |  |
|  | 1) 600-2C10 | C | 2 | 1 | (M)(O) RH FCV may be inoperative provided: Valve is secured CLOSED, RH pack is selected OFF, Opposite Air Conditioning Pack is operative, Operations are conducted at or below FL 310, Ram Air SOV is either verified operative or deactivated OPEN, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 1 | (M)(O) LH FCV may be inoperative provided: Valve is secured CLOSED, LH pack is selected OFF, Opposite Air Conditioning Pack is operative, Operations are conducted at or below FL 310, Ram Air SOV is verified operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-15 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | Flow Control Valve (FCV) (cont’d) |  |  |  |  |  |
|  | 1) 600-2C10 (cont’d) | C | 2 | 0 | (M)(O) Both FCVs may be inoperative provided: Both valves are secured CLOSED, Both Air Conditioning Packs are selected OFF, Ram Air SOV is either verified operative or deactivated OPEN, Operations are conducted unpressurized at or below 10000 ft. MSL, Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and Extended overwater operations are prohibited. |  |
|  | 2) 600-2D15, 600-2D24 | C | 2 | 1 | (M)(O) RH FCV may be inoperative provided: Valve is secured CLOSED, RH pack is selected OFF, Opposite Air Conditioning Pack is operative, Operations are conducted at or below FL 250, Ram Air SOV is either verified operative or deactivated OPEN, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  | C | 2 | 1 | (M)(O) LH FCV may be inoperative provided: Valve is secured CLOSED, LH pack is selected OFF, Opposite Air Conditioning Pack is operative, Operations are conducted at or below FL 250, Ram Air SOV is verified operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-16 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | Flow Control Valve (FCV) (cont’d) |  |  |  |  |  |
|  | 2) 600-2D15, 600-2D24 (cont’d) | C | 2 | 0 | (M)(O) Both FCVs may be inoperative provided: Both valves are secured CLOSED, Both Air Conditioning Packs are selected OFF, Ram Air SOV is either verified operative or deactivated OPEN, Inlet Cargo Air SOV is operative or secured CLOSED, AIR CONDITIONING Cargo switch is selected to OFF, Live animals are not carried in cargo compartment, Operations are conducted unpressurized at or below 10000 ft. MSL, Procedures are established and used to ensure the cargo compartment remains empty, or are verified to contain only empty cargo handling equipment, ballast (ballast may be loaded in ULDs), and/or Fly Away Kits, and Extended overwater operations are prohibited. NOTE: Operator MELs must define which items are approved for inclusion in the Fly Away Kits, and which materials can be used as ballast. |  |
|  | 3) 600-2E25 | C | 2 | 2 | Must be operative for dispatch | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-17 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-03 | Air Conditioning Pack “FAULT/OFF” Switch Lights (light function only) | C | 2 | 0 |  |  |
| 51-04 | Air Conditioning System |  |  |  |  |  |
|  | 1) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “L PACK FAULT” and/or “R PACK FAULT” status message(s) provided: Associated pack discharge pressure sensor(s) is verified operative once each flight day, and Automatic Mode of the associated Cockpit/Cabin Temperature Control System is operative and associated MAN mode is not selected. NOTE: Pack Discharge Temperature Readout(s) and/or Cockpit TEMP Readout(s) and/or Cabin TEMP Readout(s) and/or Cockpit SEL Readout(s) and/or Cabin SEL Readout(s) may be replaced by amber dashes on the EICAS ECS Synoptic Page. |  |
|  | 2) 600-2E25 | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “L PACK FAULT” and/or “R PACK FAULT” status message(s) provided: Associated pack discharge pressure sensor(s) is verified operative once each flight day, Automatic Mode of the associated Cockpit/Cabin Temperature Control System is operative and associated MAN mode is not selected, and Both Air Conditioning Packs are selected ON. NOTE: Pack Discharge Temperature Readout(s) and/or Cockpit TEMP Readout(s) and/or Cabin TEMP Readout(s) and/or Cockpit SEL Readout(s) and/or Cabin SEL Readout(s) may be replaced by amber dashes on the EICAS ECS Synoptic Page. (cont’d) | ¦¦¦¦¦¦¦¦¦¦¦¦¦¦¦¦¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-18 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-04 | Air Conditioning System (cont’d) |  |  |  |  |  |
|  | 3) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 1 | System redundancy may be degraded as indicated by “L PACK FAULT” and/or “R PACK FAULT” status messages provided the associated Air Conditioning Pack(s) is considered inoperative. |  |
| 51-05 | Pack Supply Pressure Indication (600-2B19) | C | 2 | 0 | (O) NOTE: Pack Supply Pressure Readout on the EICAS ECS Synoptic Page will be replaced by amber dashes and the pack flowline will be black with white outlines. |  |
| 52-01 | Ram Air SOV |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, RH Air Conditioning Pack is operative, LH Air Conditioning Pack is selected OFF, and Operations are conducted at or below FL 250. NOTE: Ground operations should be limited at ambient temperatures greater than 30 degrees Celsius, to prolong service life of avionics components. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-19 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 52-01 | Ram Air SOV (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (cont’d) | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, LH Air Conditioning Pack is selected OFF, Operations are conducted unpressurized at or below 10000 ft. MSL, EMER DEPRESS switch is selected ON, Overboard Exhaust SOV (Avionics Cooling) is secured OPEN, and Extended Overwater operations are prohibited. NOTE: Ground operations should be limited at ambient temperatures greater than 30 degrees Celsius, to prolong service life of avionics components. |  |
|  | 2) 600-2C10 | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, LH Air Conditioning Pack is operative, RH Air Conditioning Pack is selected OFF, Operations are conducted at or below FL 310, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-20 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 52-01 | Ram Air SOV (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10 (cont’d) | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, RH and LH Air Conditioning Packs are selected OFF, Operations are conducted unpressurized at or below 10000 ft. MSL, Cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and EMER DEPRESS switch is selected ON. |  |
|  | 3) 600-2D15, 600-2D24 | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, LH Air Conditioning Pack is operative, RH Air Conditioning Pack is selected OFF, Operations are conducted at or below FL 250, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-21 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 52-01 | Ram Air SOV (cont’d) |  |  |  |  |  |
|  | 3) 600-2D15, 600-2D24 (cont’d) |  | 1 | 0 | (M)(O) May be inoperative OPEN provided: Ram Air SOV is deactivated OPEN, RH and LH Air Conditioning Packs are selected OFF, Inlet Cargo Air SOV is operative or secured CLOSED, AIR CONDITIONING Cargo switch is selected to OFF, Live animals are not carried in cargo compartment, Operations are conducted unpressurized at or below 10000 ft. MSL, Procedures are established and used to ensure the cargo compartments remain empty, or are verified to contain only empty cargo handling equipment, ballast (ballast may be loaded in ULDs), and/or Fly Away Kits, and EMER DEPRESS switch is selected ON. NOTE: Operator MELs must define which items are approved for inclusion in the Fly Away Kits, and which materials can be used as ballast. |  |
|  | 4) 600-2E25 | C | 1 | 1 | Must be operative for dispatch | ¦ |
| 52-02 | Air Conditioning Panel RAM AIR “OPEN” Switchlight (light function only) | C | 1 | 0 |  |  |
| 52-03 | Ram Air Regulating Valve (RARV) |  |  |  |  |  |
|  | 1) 600-2D15, 600-2D24 | C | 2 | 1 | One may be inoperative provided associated Air Conditioning Pack is considered inoperative. | ¦¦ |
|  | 2) 600-2E25 | C | 2 | 2 | Must be operative for dispatch. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-22 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 55-01 | Cargo Conditioned Air SOV *** (600-2B19) | D | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  |  | D | 1 | 0 | May be inoperative OPEN provided: Cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and AIR CONDITIONING Cargo switch is selected to OFF. |  |
| 55-02 | Cargo Fan *** (600-2B19) | D | 1 | 0 | (M) May be inoperative provided live animals are not carried in cargo compartment. |  |
| 55-03 | Cargo Exhaust SOV |  |  |  |  |  |
|  | 1) 600-2B19 *** | D | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  |  | D | 1 | 0 | May be inoperative OPEN provided: Cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  |  |  |  |  | cont’d |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-23 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 55-03 | Cargo Exhaust SOV (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to OFF. | ¦ |
|  |  | C | 1 | 0 | May be inoperative OPEN provided: Aft cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and AIR CONDITIONING Cargo switch is selected to OFF. |  |
| 55-04 | Cargo Air SOV |  |  |  |  |  |
|  | 1) Recirculated *** (600-2B19) | D | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to COND AIR or OFF. |  |
|  |  | D | 1 | 0 | May be inoperative OPEN provided: Cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  |  |  |  |  | cont’d |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-24 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 55-04 | Cargo Air SOV (cont’d) |  |  |  |  |  |
|  | 2) Inlet (600-2C10) | C | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  |  | C | 1 | 0 | May be inoperative OPEN provided: Aft cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), and AIR CONDITIONING Cargo switch is selected to OFF. |  |
|  | 3) Inlet (600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative CLOSED provided: SOV is secured CLOSED, Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to OFF. | ¦ |
|  |  | C | 1 | 0 | May be inoperative OPEN provided: Aft cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable), AIR CONDITIONING Cargo switch is selected to OFF, Both Recirculation Fans are operative, Both Air Conditioning Packs are operative, Both Flow Control Valves are operative, Both Pressure Regulating SOVs are operative, and Both High Pressure Valves are operative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-25 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 55-05 | AFT Cargo Compartment Temperature Control System *** |  |  |  |  |  |
|  | 1) 600-2B19 | D | 1 | 0 | May be inoperative provided: Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to FAN or OFF. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | D | 1 | 0 | May be inoperative provided: Live animals are not carried in cargo compartment, and AIR CONDITIONING Cargo switch is selected to AIR or OFF. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-26 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 61-01 | Cabin/Cockpit Temperature Control Systems |  |  |  |  |  |
|  | 1) Automatic Mode | C | 2 | 1 | (M) One automatic control may be inoperative provided: Associated Manual control is operative, and Associated Duct Temperature Indication is operative. |  |
|  |  | C | 2 | 0 | (M) Both automatic controls may be inoperative provided: Both Manual controls are operative, and Both Duct Temperature Indications are operative. |  |
|  | 2) Manual Mode | C | 2 | 1 | (M) One manual control may be inoperative provided: Associated Automatic control is operative, and Associated Duct Temperature Indication is operative. |  |
|  |  | C | 2 | 0 | (M) Both manual controls may be inoperative provided: Both Automatic controls are operative, and Both Duct Temperature Indications are operative. |  |
|  | 3) 600-2B19, 600-2C10, 600-2D15, 600-2D24 | C | 2 | 1 | (O) One may be inoperative provided associated Air Conditioning Pack is considered inoperative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-27 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 61-02 | EICAS “CABIN TEMP” Indication (600-2B19) | C | 1 | 0 |  |  |
|  | 1) Upper Cabin Temperature Sensor (A/c with SB 601R-21-039) | D | 1 | 0 | May be inoperative provided indication is switched to Lower Cabin Temperature Sensor. |  |
|  | 2) Lower Cabin Temperature Sensor (A/c with SB 601R-21-039) | D | 1 | 0 | May be inoperative provided indication is switched to Upper Cabin Temperature Sensor. |  |
| 61-03 | Duct Temperature Indications (COCKPIT and CABIN) (600-2B19) | C | 2 | 0 | Both may be inoperative provided associated Cockpit and/or Cabin Automatic Temperature Control Mode is operative. |  |
| 61-04 | Air Conditioning Panel CKPT/CABIN Temperature Control “MAN” Switch Lights (light function only) | C | 2 | 0 |  |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 21-28 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 21 – AIR CONDITIONING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 22-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 22 – AUTO FLIGHT |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Autopilot System | C | 1 | 0 | Except where enroute operations or approach procedures require its use, may be inoperative provided Altitude Alerting system is operative. NOTE 1: Autopilot is required for RVSM Operations. NOTE 2: Relief for inoperative individual flight guidance operational modes is provided by MMEL Item 22-10-02 Flight Directors. |  |
| 10-02 | Flight Directors |  |  |  |  |  |
|  | 600-2B19, 600-2C10, 600-2D15, 600-2D24 | C | 2 | 1 | (O) Except where enroute operations or approach procedures require its use, may be inoperative provided Autopilot is considered inoperative. NOTE 1: Windshear escape guidance function will be available from the remaining Flight Director. NOTE 2: The TOGA switches will not be affected by the inoperative Flight Director. NOTE 3: Although take-off configuration warning system remains operative, “T/O CONFIG OK” advisory message is inhibited. | ¦¦¦ ¦¦ ¦¦ ¦¦¦ |
|  | 600-2E25 | C | 2 | 1 | (O) Except where enroute operations or approach procedures require its use, may be inoperative provided: Autopilot is considered inoperative, and Pilot with the operative Flight Director performs the take off. NOTE 1: Windshear escape guidance function will be available from the remaining Flight Director. NOTE 2: The TOGA switches will not be affected by the inoperative Flight Director. NOTE 3: Although take-off configuration warning system remains operative, “T/O CONFIG OK” advisory message is inhibited. | ¦¦¦ ¦¦ ¦¦¦ ¦¦¦¦¦¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 22-2 ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 22 – AUTO FLIGHT |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-02 | Flight Directors (cont’d) |  |  |  |  |  |
|  | 600-2B19, 600-2C10, 600-2D15, 600-2D24 | C | 2 | 0 | (O) Except where enroute operations or approach procedures require its use, may be inoperative provided: Autopilot is considered inoperative, and TOGA switches are considered inoperative. NOTE 1: Windshear escape guidance will be inoperative. However, all remaining windshear functions will be available. NOTE 2: Although take-off configuration warning system remains operative, “T/O CONFIG OK” advisory message is inhibited. | ¦¦¦ ¦¦ ¦¦¦ ¦¦¦ |
|  | Flight Director Modes | C | - | - | Except where enroute operations or approach procedures require its use, individual flight director modes may be inoperative provided Altitude Alerting System is operative. NOTE 1: Flight director altitude hold mode is required for RVSM Operations. NOTE 2: Any flight director mode which operates normally may be used. | ¦¦¦¦ ¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 22-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 22 – AUTO FLIGHT |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Autopilot Disconnect Switches (Control Wheel) | C | 2 | 1 | (O) One may be inoperative provided: Autopilot is not used below 1,500 ft AGL, Approach mimimums do not require the use of autopilot, and Pilot flying has the operative disconnect. | ¦ ¦ ¦¦ ¦ |
|  |  | B | 2 | 0 | (O) May be inoperative provided the autopilot is not used. | ¦¦ |
| 11-02 | Flight Director Sync Switches | C | 2 | 0 |  |  |
| 11-03 | Take-Off/Go-Around (TOGA) Switches (on Thrust Levers) |  |  |  |  |  |
|  | 600-2B19, 600-2C10, 600-2D15, 600-2D24 | C | 2 | 0 | (O) Both may be inoperative provided Alternate procedures are established and used. NOTE 1: All normal flight director modes are available. NOTE 2: Windshear escape guidance is not affected by the loss of the TOGA function and remains operative during the approach and take off phases of flight. |  |
|  | 600-2E25 | C | 2 | 1 | (O) May be inoperative provided: Alternate procedures are established and used, and Pilot with the operative TOGA switch performs the take off. NOTE 1: All normal flight director modes are available. NOTE 2: Windshear escape guidance is not affected by the loss of the TOGA function and remains operative during the approach and take off phases of flight. | ¦¦¦¦¦¦¦¦¦¦¦¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 22-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 22 – AUTO FLIGHT |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | V-Speed Auto-Synchronization System | C | 1 | 0 | May be inoperative provided V-Speed settings are made manually by each pilot. |  |
| 12-02 | Integrated Avionics Processor System (IAPS) Input/Output Concentrator (IOC) |  |  |  |  |  |
|  | 600-2B19 | C | 4 | 3 | (M) One IAPS IOC may be inoperative provided remaining IOCs are verified operative before the first flight of the day. NOTE 1: “IAPS DEGRADED” status message will be displayed on EICAS. NOTE 2: Although take-off configuration warning system remains operative, “T/O CONFIG OK” advisory message is inhibited. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 4 | 3 | (M)(O) One IAPS IOC may be inoperative provided remaining IOCs are verified operative before the first flight of the day. NOTE 1: “IAPS DEGRADED” status message will be displayed on EICAS. | ¦ |
| 21-01 | Mach Trim System | C | 1 | 0 | Except where enroute operations require its use, may be inoperative provided operations are conducted at or below 250 KIAS/ .7 M when autopilot is disengaged. |  |
| 22-01 | Yaw Dampers (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | (M) May be inoperative provided the affected damper is verified not engaged. | ¦ |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | VHF Communication Systems | D | - | - | Any in excess of those required by Regulations may be inoperative provided it is not powered by the Battery Bus and not required for emergency procedures. |  |
| 12-01 | HF Communication Systems *** | D | - | - | Any in excess of those required by Regulations may be inoperative. |  |
| 21-01 | Selective Call System (SELCAL) *** | C | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 1 | 0 | May be inoperative provided procedures do not require its use. |  |
|  | Channels | C | 4 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 4 | 0 | May be inoperative provided procedures do not require its use. |  |
| 22-01 | Aircraft Communications Addressing and Reporting System (ACARS) *** | C | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 1 | 0 | May be inoperative provided routine procedures do not require its use. |  |
| 22-02 | AFIS (Automatic Flight Information System) *** | C | - | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
| 22-03 | Printer *** | C | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 1 | 0 | May be inoperative provided routine procedures do not require its use. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Passenger Address System | A | 1 | 0 | (O) May be inoperative provided: Aircraft crew are the only occupants of the aircraft, Alternate procedures are established and used, and Repairs are made within one flight day. NOTE: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. |  |
|  | 1) 600-2B19 | B | 1 | 0 | (O) May be inoperative provided: Flight Attendant Call Switch Lights and Flight Attendant Audio Alerting System of Crewmember Interphone System are operative, and Alternate, normal and emergency procedures are established and used. NOTE: Any station function(s) that operates normally may be used. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Passenger Address System (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (cont’d) |  |  |  |  |  |
|  | a) Passenger Address “PA” Switch Lights (Interphone Control Unit and Flight Attendant Station) (light function only) | C | - | 0 | (O) May be inoperative provided: Flight Attendant Call Switch Lights and Flight Attendant Audio Alerting System of Crewmember Interphone System are operative, and Alternate, normal and emergency procedures are established and used. NOTE: Any station function(s) that operates normally may be used. |  |
|  | b) Lavatory Speakers | C | - | 0 | (O) Alternate, normal and emergency procedures are established and used. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Passenger Address System (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 1 | 0 | (O) May be inoperative provided: Flight Attendant Call Switch Lights and Flight Attendant Audio Alerting System of Crewmember Interphone System are operative, Megaphone(s) is/are readily available and operates normally, and Alternate, normal and emergency procedures are established and used. NOTE: Any station function(s) that operates normally may be used. | ¦ |
|  | a) Passenger Address “PA” Switch Lights (Interphone Control Unit and Flight Attendant Station) (light function only) | C | 3 | 0 | (O) May be inoperative provided: Flight Attendant Call Switch Lights and Flight Attendant Audio Alerting System of Crewmember Interphone System are operative, Megaphone(s) is/are readily available and operates normally, and Alternate, normal and emergency procedures are established and used. NOTE: Any station function(s) that operates normally may be used. |  |
|  | b) Lavatory Speakers | C | - | 0 | (O) Alternate, normal and emergency procedures are established and used. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-02 | Flight Attendant Handsets | B | - | 1 | (O) May be inoperative provided: Operative handset is located at an operative Flight Attendant Seat Assembly, and Alternate communications procedures for affected flight attendant station are established and used. NOTE: Any handset function(s) that operates normally may be used. |  |
| 32-01 | Prerecorded Announcement and Boarding Music System *** | D | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
| 40-01 | Crewmember Interphone System |  |  |  |  |  |
|  | 1) Interphone Voice Communication Function |  |  |  |  |  |
|  | a) Flight Deck to Cabin (Audio Control Panel(s) to Cabin) | B | 3 | 1 | (O) May be inoperative provided: Either pilot or co-pilot flight deck to cabin interphone voice communication function (two way) operates normally, Passenger Address System is verified operative prior to each flight, and Alternate procedures for communication with cabin are established and used. NOTE: Any station function(s) that operates normally may be used. | ¦¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-6 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | Crewmember Interphone System (cont’d) |  |  |  |  |  |
|  | 1) Interphone Voice Communication Function (cont’d) |  |  |  |  |  |
|  | b) Cabin to Flight Deck (Flight Attendant Station(s) to Flight Deck) | B | - | 1 | (O) May be inoperative provided: Cabin to flight deck interphone voice communication function (two way) operates normally at least at one flight attendant station, Unaffected flight attendant station(s) has an operative Flight Attendant Seat Assembly, Unaffected flight attendant station(s) has an operative Flight Attendant Handset, and Alternate communication procedures for the affected flight attendant station(s) are established and used. NOTE: Any station function(s) that operates normally may be used. |  |
|  | c) Cabin to Cabin (Flight Attendant Station(s) to Flight Attendant Station(s)) | B | - | 0 | (O) May be inoperative provided alternate communication procedures for the affected flight attendant station(s) are established and used. NOTE: Any station function(s) that operates normally may be used. |  |
|  | d) Flight Deck to Ground (Audio Contro Panel(s) to Ground)l | C | 3 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 3 | 0 | May be inoperative provided procedures do not require its use. NOTE: Any station function(s) that operates normally may be used. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-7 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | Crewmember Interphone System (cont’d) |  |  |  |  |  |
|  | 1) Interphone Voice Communication Function (cont’d) |  |  |  |  |  |
|  | e) Ground to Flight Deck (Maintenance | C | 4 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  | Interphone Station(s) to Flight Deck) | D | 4 | 0 | May be inoperative provided procedures do not require its use. NOTE: Any station function(s) that operates normally may be used. |  |
|  | 2) Interphone Alerting Function |  |  |  |  |  |
|  | a) Flight Deck Call Switch Lights (“CALL” and “EMER”) (600-2B19) | B | 2 | 0 | May be inoperative provided the flight compartment audio alerting system (chime) is operative. NOTE 1: Flight deck audio alerting system (chime) must always be operative. NOTE 2: Any Flight Deck Call Switch Light function(s) that operates normally may be used. |  |
|  | b) Flight Deck Call Switch Lights (“CALL” and “EMER”) (light function only) (600-2C10, 600-2D15, 600-2D24, 600-2E25) | B | 2 | 0 | May be inoperative provided the flight compartment audio alerting system (chime) is operative. NOTE 1: Flight deck audio alerting system (chime) must always be operative. NOTE 2: Any Flight Deck Call Switch Light function(s) that operates normally may be used. | ¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-8 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | Crewmember Interphone System (cont’d) |  |  |  |  |  |
|  | 2) Interphone Alerting Function (cont’d) |  |  |  |  |  |
|  | c) Flight Attendant Call Switch Lights (“ATT”, “FLT” and “EMG”) (light function only) | B | 3 | 0 | (O) May be inoperative provided Passenger Address System is operative. NOTE: Any Flight Attendant Call Switch Light function(s) that operates normally may be used. |  |
|  | d) Mid Cabin Flight Attendant Call Lights (Cockpit, Lavatory, Cabin) | B | 6 | 0 | (O) May be inoperative provided Passenger Address System is operative. NOTE: Any Flight Attendant Call Switch Light function(s) that operates normally may be used. |  |
|  | e) Flight Attendant Audio Alerting System (Chime) | B | 1 | 0 | May be inoperative provided Passenger Address System is operative. |  |
|  | f) Mechanic Call Switch Lights (CKPT “CALL” and MECH “CALL”) | C | 2 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
|  |  | D | 2 | 0 | May be inoperative provided procedures do not require its use. NOTE: Any Mechanic Call Switch Light function(s) that operates normally may be used. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-9 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Hand Held Microphones | C | 2 | 1 | One may be inoperative provided associated Boom Microphone is operative and is used. |  |
|  |  | C | 2 | 0 | Both may be inoperative provided: Boom Microphones are operative, and Spare boom microphone is available in flight compartment. |  |
| 51-02 | RT/IC Switches |  |  |  |  |  |
|  | 1) Pilot’s/Copilot’s RT/IC Switches | C | 4 | 2 | Two may be inoperative provided: Switch is not failed in transmit mode, One RT/IC switch operates normally for each crew-member, and Hand Held Microphone on affected side is operative. |  |
|  | 2) Observer’s RT/IC Switch | B | 1 | 0 | May be inoperative provided: Switch is not failed in transmit mode, and Observer’s Seat is considered inoperative. |  |
| 51-03 | Flight Compartment Speakers | C | 2 | 0 | Both may be inoperative provided all flightcrew members on flight deck duty utilize headsets. |  |
| 51-04 | Boom Microphones | A | - | 0 | May be inoperative provided: Flight Data Recorder is operative, and Repairs are made within three flight days. |  |
| 51-05 | Headsets (600-2B19 with both S.B.s 601R-23-004 and 601R-34-013), (600-2C10, 600-2D15, 600-2D24, 600-2E25) | D | - | - | Any in excess of those required for each person on flight compartment duty may be inoperative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-10 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-06 | Observer’s Audio Control Panel | B | 1 | 0 | May be inoperative provided Observer’s Seat is considered inoperative. |  |
| 71-01 | Cockpit Voice Recorder (CVR) | A | 1 | 0 | May be inoperative provided: Flight Data Recorder is operative, and Repairs are made within three flight days. |  |
| 81-01 | #2 Radio Tuning Unit (RTU) |  |  |  |  |  |
|  | (600-2B19), (600-2C10, 600-2D15, 600-2D24 without Modsum 670T122173 or 670T31608) | C | 1 | 0 | May be inoperative provided: COM/NAV tuning unit is operative, Cross-side tuning from RTU#1 is operative, For single HF installation, operations do not require the use of HF, and RTU #2 is de-selected using its RTU INHIBIT switch to ensure cross-side tuning by RTU #1. NOTE: If RTU #1 fails, all RTU mode selections (COM 1 Squelch ON/OFF, NAV1 Marker sens. LO/HI, NAV1 DME-HOLD, ATC Altitude ON-OFF, ATC ID, ADF ANT, ADF BFO (ON/OFF), TCAS) and HF tuning will be lost; however COM1/NAV1 frequency tuning will be available through the COM/NAV tuning unit and VHF2, NAV2, ADF1 & ADF2 tuning and ATC code will be available if FMS burst tuning is available. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-11 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 81-01 | #2 Radio Tuning Unit (RTU) (cont’d) |  |  |  |  |  |
|  | (600-2B19), (600-2C10, 600-2D15, 600-2D24 without Modsum 670T122173 or 670T31608) (cont’d) | C | 1 | 0 | (O) May be inoperative provided: Burst tuning control on at least one FMS is operative, Cross-side tuning from RTU#1 is operative, For single HF installation, operations do not require the use of HF, and RTU #2 is de-selected using its RTU INHIBIT switch to ensure cross-side tuning by RTU #1. NOTE: If RTU #1 fails, all RTU mode selections (COM 1 Squelch ON/OFF, NAV1 Marker sens. LO/HI, NAV1 DME-HOLD, ATC Altitude ON-OFF, ATC ID, ADF ANT, ADF BFO (ON/OFF), TCAS) and HF tuning will be lost; however COM/NAV/ADF frequency tuning and ATC code will be available through FMS. |  |
|  | (600-2C10, 600-2D15, 600-2D24 with Modsum 670T122173 or 670T31608) (600-2E25) | C | 1 | 0 | (O) May be inoperative provided: Cross-side tuning from RTU#1 is operative, Burst tuning control on at least one FMS is operative, For single HF installation, operations do not require the use of HF, and RTU #2 is de-selected using its RTU INHIBIT switch to ensure cross-side tuning by RTU #1. NOTE: If RTU #1 fails, all RTU mode selections (COM 1 Squelch ON/OFF, NAV1 Marker sens. LO/HI, NAV1 DME-HOLD, ATC Altitude ON-OFF, ATC ID, ADF ANT, ADF BFO (ON/OFF), TCAS and HF tuning) will be lost; however COM/NAV/ADF frequency tuning and ATC code will be available through FMS. | ¦ |
| Aircraft – Aéronef | Revision No – No de evision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 23-12 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 23 – COMMUNICATIONS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 82-01 | COM/NAV Standby Tuning Unit (600-2B19), (600-2C10, 600-2D15, 600-2D24 without Modsum 670T122173 or 670T31608) | C | 1 | 0 | May be inoperative provided RTU #2 is operative. |  |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Burst tuning control on at least one FMS is operative, and FMS TUNE INHIBIT Switch is operative. |  |
| 82-02 | FMS TUNE INHIBIT Switch (600-2B19, 600-2C10, 600-2D15, 600-2D24) | C | 1 | 0 | May be inoperative in ON (INHIBIT) position provided both RTUs are operative. NOTE: Tuning function of the FMS will be inhibited. FMS navigation performance may be degraded if GPS is not available. | ¦¦¦¦ |
|  | (600-2B19), (600-2C10, 600-2D15, 600-2D24 without Modsum 670T122173 or 670T31608) | C | 1 | 0 | May be inoperative in ON (INHIBIT) position provided COM/NAV Standby Tuning Unit is operative. NOTE: Tuning function of the FMS will be inhibited. FMS navigation performance may be degraded if GPS is not available. |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Integrated Drive Generator (IDG) Systems |  |  |  |  |  |
|  | 1) Constant Speed Drives (CSD), Generator Control Unit (GCU) (600-2B19) | A | 2 | 1 | (M)(O) One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, Respective IDG is disconnected, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, APU Battery is operative, APU Battery Charger is operative, Cross-side Hydraulic Motor Pump (ACMP) is selected ON, Same side Hydraulic AC Motor Pump (ACMP) is operative, Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative), and Repairs are made after one flight. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-2 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Integrated Drive Generator (IDG) Systems (cont’d) |  |  |  |  |  |
|  | 1) Constant Speed Drives (CSD), Generator Control Unit (GCU) (600-2B19) |  |  |  |  |  |
|  | (cont’d) | A | 2 | 1 | (M)(O) One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, Respective IDG is disconnected, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, APU Battery is operative, APU Battery Charger is operative, Cross-side Hydraulic AC Motor Pump (ACMP) is considered inoperative, Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative), and Repairs are made within 30 flight hours (cumulative). |  |
|  | 2) Constant Speed Drives (CSD), Generator Control Unit (GCU) (600-2C10, 600-2D15, 600-2D24, 600-2E25) | A | 2 | 1 | (O) One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, Respective IDG is disconnected, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, Operations are conducted at or below FL 260, and Repairs are made within 100 flight hours (cumulative). (cont’d) | ¦ |
| Aircraft – Aéronef | Revision No – No de evision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Integrated Drive Generator (IDG) Systems (cont’d) |  |  |  |  |  |
|  | 3) Generators (600-2B19) | A | 2 | 1 | (M)(O) One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, APU Battery is operative, APU Battery Charger is operative, Cross-side Hydraulic AC Motor Pump (ACMP) is selected ON, Same side Hydraulic AC Motor Pump (ACMP) is operative, Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative), and Repairs are made after one flight. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-4 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Integrated Drive Generator (IDG) Systems (cont’d) |  |  |  |  |  |
|  | 3) Generators (600-2B19) (cont’d) |  |  |  |  |  |
|  |  | B | 2 | 1 | (M) One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, APU Battery is operative, APU Battery Charger is operative, Cross-side Hydraulic AC Motor Pump (ACMP) is considered inoperative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 4) Generators (600-2C10, 600-2D15, 600-2D24, 600-2E25) | B | 2 | 1 | One may be inoperative provided: Respective GEN 1(2) switch is selected to OFF/RESET, APU generator is operated continuously throughout flight, AFM performance corrections for APU ON are applied, and Operations are conducted at or below FL 260. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-5 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-02 | IDG 1(2) “FAULT/DISC” Switch Lights (light function only) | C | 2 | 0 |  |  |
| 22-01 | APU Generator System | C | 1 | 0 | May be inoperative provided: a) IDG 1 and IDG 2 are operative, and b) APU GEN switch is selected to OFF/RESET. |  |
| 23-01 | Air Driven Generator (ADG) Auto-deploy System | C | 1 | 0 | (M) May be inoperative provided system is deactivated. |  |
|  | ADG Deployment Squib (600-2B19 without ModSum TC 601R14177 (wet ADG)) | C | 1 | 0 | (M) May be inoperative provided Deployment Squib is deactivated. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-6 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-01 | AUTO XFER “FAIL/OFF” Switch Lights (light function only) | C | 2 | 0 |  |  |
| 31-01 | Transformer Rectifier Units (TRUs) |  |  |  |  |  |
|  | 1) 600-2B19 | B | 5 | 4 | (M)(O) One may be inoperative provided ESS TRU 1 and TRU 1 are operative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 4 | 3 | (M) | ¦ |
| 31-02 | TRU Cooling Fans |  |  |  |  |  |
|  | 1) 600-2B19 | C | 5 | 3 | (M) One or two cooling fans may be inoperative provided: One ESS TRU Cooling Fan is operative, and Forward equipment doors are OPENED for stationary ground operations at temps. >30 °C. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 4 | 0 | (M) | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-7 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-01 | Main Battery |  |  |  |  |  |
|  | 1) 600-2B19 (AHRS equipped aircraft or aircraft with ModSum TC601R15209) | A | 1 | 0 | (M)(O) May be inoperative provided: APU air intake door is secured fully OPEN, AFM performance corrections for APU ON are applied, APU is operated continuously during flight or aircraft speed is limited to 300 KIAS if APU is OFF, APU battery is operative, APU battery charger is operative, APR is selected OFF, Operations are conducted in accordance with AFM APR OFF performance data, Service Lights are considered inoperative, Maintenance Lights are considered inoperative, A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE 1: DG mode heading slew function will be inoperative. NOTE 2: Clocks will be inoperative. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-8 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-01 | Main Battery (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (AHRS equipped aircraft or aircraft with ModSum TC601R15209) (cont’d) | A | 1 | 0 | (M)(O) May be inoperative provided: APU air intake door is secured fully CLOSED, APU is considered inoperative, APU battery is operative, APU battery charger is operative, APR is selected OFF, Operations are conducted in accordance with AFM APR OFF performance data, Service Lights are considered inoperative, Maintenance Lights are considered inoperative, A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE 1: DG mode heading slew function will be inoperative. NOTE 2: Clocks will be inoperative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 1 | 0 | (M) May be inoperative provided: A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE: Clocks will be inoperative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-9 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-02 | Main Battery Charger |  |  |  |  |  |
|  | 1) 600-2B19 (AHRS equipped aircraft or aircraft with ModSum TC601R15209) | A | 1 | 0 | (M)(O) May be inoperative provided: Main Battery is considered inoperative, APU air intake door is secured fully OPEN, APU is operated continuously during flight or the aircraft speed is limited to 300 KIAS if APU is OFF, AFM performance corrections for APU ON are applied, APU Battery is operative, APU Battery charger is operative, APR is selected OFF, Operations are conducted in accordance with AFM APR OFF performance data, Service Lights are considered inoperative, Maintenance Lights are considered inoperative, A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE 1: DG mode heading slew function will be inoperative. NOTE 2: Clocks will be inoperative. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-10 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-02 | Main Battery Charger (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (AHRS equipped aircraft or aircraft with ModSum TC601R15209) | A | 1 | 0 | (M)(O) May be inoperative provided: Main Battery is considered inoperative, APU air intake door is secured fully CLOSED, APU is considered inoperative, APU Battery is operative, APU Battery charger is operative, APR is selected OFF, Operations are conducted in accordance with AFM APR OFF performance data, Service Lights are considered inoperative, Maintenance Lights are considered inoperative, A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE 1: DG mode heading slew function will be inoperative. NOTE 2: Clocks will be inoperative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 1 | 0 | (M) May be inoperative provided: Main Battery is considered inoperative, A reliable and functioning time-piece is readily available (a wristwatch is acceptable), Flight Data Recorder is considered inoperative, and Repairs are made within one flight day. NOTE: Clocks will be inoperative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-11 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 32-03 | APU Battery (600-2B19) | A | 1 | 0 | (M) May be inoperative provided: Main Battery is operative, Main Battery Charger is operative, AFM performance corrections for APU ON are applied when APU is used, and Repairs are made within one flight day. NOTE: External DC power will be required to start the APU and for pressure refueling. |  |
| 32-04 | APU Battery Charger (600-2B19) | A | 1 | 0 | (M) May be inoperative provided: Main Battery is operative, Main Battery Charger is operative, APU Battery is considered inoperative after the APU is started, AFM performance corrections for APU ON are applied when APU is used, and Repairs are made within one flight day. NOTE: External DC power will be required to start the APU and for pressure refueling. |  |
| 33-01 | DC TIE 1/ 2 “CLOSED” Switch Lights (light function only) (600-2B19) | C | 2 | 0 |  |  |
| 33-02 | DC “ESS TIE CLOSED” Switch Lights (light function only) (600-2B19) | C | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-12 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-01 | External AC Power “AVAIL/ IN USE” Switch Light (Overhead Panel) (light function only) | C | 1 | 0 |  |  |
| 41-02 | External AC Power “AVAIL/ IN USE” Switch Light (Service Panel) (light function only) | C | 1 | 0 |  |  |
| 41-03 | External AC Power System | C | 1 | 0 |  |  |
| 42-01 | External DC Power “AVAIL/ IN USE” Switch Light (light function only) (600-2B19) | C | 1 | 0 |  |  |
| 42-02 | External DC Power System (600-2B19) | C | 1 | 0 |  |  |
| 50-01 | AC Service Bus (600-2B19) | C | 1 | 0 | (M) May be inoperative provided: Lavatory door is locked CLOSED and placarded “INOPERATIVE – DO NOT ENTER”, Lavatory is not used for any purpose, and DC “ESS TIE” switch light is selected CLOSED. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-13 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 50-02 | Synoptic Page AC Service Bus Indication (600-2B19) | C | 1 | 0 | May be inoperative provided: “DC TIE ½” and “DC ESS TIE” are not displayed on EICAS, and DC SERVICE BUS on EICAS is powered normally. |  |
| 50-03 | Load Shedding System *** (600-2C10, 600-2D15, 600-2D24 600-2E25) | D | 1 | 0 |  | ¦ |
| 51-01 | AC ESS XFER “ALTN” Switch Light (light function only) | C | 1 | 0 |  |  |
| 51-02 | AC Essential Power Transfer Relay (K3XD) (600-2B19) | B | 1 | 0 | May be inoperative provided: a) IDG1 and IDG2 are operative, b) ESS TRU 2 is operative, and c) EICAS “AC ESS BUS” caution message is not displayed. |  |
| 61-02 | DC Utility Bus (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided cabin right side reading lights are considered inoperative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 24-14 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 24 – ELECTRICAL POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 00-01 | “Fasten Seat Belt While Seated” Placards | C | - | - | One or more placards may be illegible or missing provided a legible sign or placard is readable from each occupied passenger seat. |  |
| 11-01 | Pilot Seats |  |  |  |  |  |
|  | 1) Lumbar Supports | C | 2 | 0 | May be inoperative in lowest position provided seat is acceptable to the affected crewmember. |  |
|  | 2) Arm Rests | C | 4 | 0 | (M) May be inoperative or missing provided: Egress is not impaired, and Seat is acceptable to affected crewmember. |  |
|  | 3) Height Adjustments | B | 2 | 0 | (M) May be inoperative provided: Seat is secured in vertical position acceptable to affected crewmember, Fore/Aft Adjustment is verified operative, Egress is not impaired, and If HGS is installed and required for flight, the vertical position of the seat must be acceptable to affected crewmember. |  |
|  | 4) Fore/Aft Adjustments | B | 2 | 0 | (M) May be inoperative provided: Seat is secured in fore/aft position acceptable to affected crewmember, Height Adjustment is verified operative, and Egress is not impaired. |  |
|  | 5) Recline Adjustments | B | 2 | 0 | May be inoperative provided backrest is secured in position acceptable to affected crewmember. |  |
|  | 6) Thigh Supports | C | 2 | 0 | May be inoperative provided seat is acceptable to affected crewmember. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-2 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 12-01 | Observer’s Seat (Including associated equipment) | B | 1 | 0 | (M) May be inoperative except when required by a person in an official capacity provided the seat is removed, stowed, or secured in the retracted position. NOTE: Associated equipment includes shoulder harness, lap belt, Audio Control Unit, RT/IC Switches, and Observer’s Oxygen System. | ¦¦¦ ¦ |
|  |  | D | 1 | 0 | (M) May be inoperative provided: The seat is not required to be occupied in a official capacity for extended periods of time, and The seat is removed, stowed, or secured in the retracted position. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 18-01 | Cockpit Sunvisors | C | 2 | 1 | May be inoperative or removed provided affected sunvisor does not obstruct either pilot’s field of view for take-off and landing. |  |
|  |  | C | 2 | 0 | May be inoperative or removed provided: Affected sunvisor does not obstruct either pilot’s field of view for take-off and landing, and Aircraft is operated at night. |  |
| 18-02 | Cockpit Chart Holders (Control Column and Window) | C | 4 | 2 | One holder may be inoperative or missing on each side provided the holder is acceptable to affected crewmember. |  |
|  |  | B | 2 | 1 | One holder may be inoperative or missing provided the EFB on the same side is operative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 21-01 | Passenger Seats | D | - | - | (O) May be inoperative provided: Seat does not block nor restrict access to an emergency exit, Seat does not restrict any passenger from access to the main aisle, and The affected seat(s) is blocked and placarded “DO NOT OCCUPY”. NOTE 1: A seat with an inoperative seat belt is considered inoperative. NOTE 2: Affected seat(s) may include the seat(s) behind and/or adjacent outboard seats. |  |
|  | 1) Recline Mechanism | C | - | - | May be inoperative and seat occupied provided seatback is immovable in full upright position. |  |
|  |  | D | - | - | (M) May be inoperative and seat occupied provided seat is secured in the up-right position. |  |
|  | 2) Under seat Baggage Restraining Bars | C | - | - | (O) May be inoperative or missing provided: Baggage is not stowed under seat or bank of seats, Seat back is placarded “DO NOT STOW BAGGAGE UNDER THIS SEAT”, Restraining bar does not restrict any passenger from access to the main aircraft aisle or emergency exit, and Procedures are established to alert crew members of an inoperative or missing restraining bar. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-5 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 21-01 | Passenger Seats (cont’d) |  |  |  |  |  |
|  | 3) Armrest |  |  |  |  |  |
|  | a) Armrest with Recline Mechanism | D | - | - | (M) May be inoperative or missing and seat occupied provided: Armrest does not block an emergency exit, Armrest does not restrict any passenger from access to the main aircraft aisle, and If armrest is missing, seat is secured in the full upright position. |  |
|  | b) Armrest without Recline Mechanism | D | - | - | May be inoperative or missing and seat occupied provided: Armrest does not block an emergency exit, and Armrest does not restrict any passenger from access to the main aircraft aisle. |  |
|  | c) Downlock Mechanism | D | - | - | May be inoperative and seat occupied provided: Armrest does not block an emergency exit, and Armrest does not restrict any passenger from access to the main aircraft aisle. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-6 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 22-01 | Flight Attendant Seat Assembly |  |  |  |  |  |
|  | 1) Required Flight Attendant Seats | B | - | 1 | (O) One seat or seat assembly may be inoperative provided: Affected seat or seat assembly is not occupied, Flight Attendant displaced by inoperative seat occupies the passenger seat which is most accessible to the inoperative seat, so as to most effectively perform assigned duties, Alternate procedures are established and used as published in crewmember manuals, Folding type seat stows automatically or is secured in the retracted position, and Passenger seat assigned to flight attendant is placarded “FOR FLIGHT ATTENDANT USE ONLY”. NOTE 1: Inoperative automatic stow feature of a folding seat renders the seat inoperative. NOTE 2: A seat with a missing or inoperative safety belt (including shoulder harness) or headrest renders the seat inoperative. |  |
|  |  | B | - | 1 | (M) One seat or seat assembly may be removed provided: Flight Attendant displaced by inoperative seat occupies the passenger seat which is most accessible to the inoperative seat, so as to most effectively perform assigned duties, Alternate procedures are established and used as published in crewmember manuals, and Passenger seat assigned to flight attendant is placarded “FOR FLIGHT ATTENDANT USE ONLY”. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-7 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 22-01 | Flight Attendant Seat Assembly (cont’d) |  |  |  |  |  |
|  | 2) Excess Flight Attendant Seats | D | - | - | (O) Seats / assemblies in excess of requirements and not assigned to a flight attendant may be inoperative provided: Affected seat or seat assembly is not occupied, Affected seat or seat assembly are placarded DO NOT OCCUPY, and Folding type seat stows automatically or is secured in the retracted position. NOTE 1: Inoperative automatic stow feature of a folding seat renders the seat inoperative. NOTE 2: A seat with a missing or inoperative safety belt (including shoulder harness) or headrest renders the seat inoperative. |  |
|  |  | D | - | - | (M) Seats / assemblies in excess of requirements and not assigned to a flight attendant may be inoperative provided it is not occupied, are placarded and are: Secured in the retracted position, or Removed. NOTE 1: Inoperative automatic stow feature of a folding seat renders the seat inoperative. NOTE 2: A seat with a missing or inoperative safety belt (including shoulder harness) or headrest renders the seat inoperative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-8 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 23-01 | Overhead Storage Bin(s) / Cabin and Galley Storage Compartments / Closets | C | - | - | (M) May be inoperative provided: Procedures are established to secure bins/compartments/closets CLOSED, Associated bin/compartment/closet is prominently placarded DO NOT USE, Any emergency equipment located in affected bin/compartment/closet is considered inoperative, and Affected bin/compartment/closet is not used for storage of any item(s) except for those permanently affixed. NOTE 1: If no partitions are installed, the entire overhead stowage compartment is considered to be one bin or compartment. NOTE 2: An inoperative lid/door latch renders the lid/door inoperative. | ¦ ¦¦ ¦¦¦ ¦ ¦ ¦ |
|  |  | C | - | - | (M)(O) May be inoperative provided: Affected bin/compartment/closet door(s) is removed, Associated bin/compartment/closet is not used for storage of any item, except those permanently affixed, Associated bin/compartment/closet is prominently placarded DO NOT USE, Procedures are established and used to alert crew members and passengers of inoperative bins/compartments/closets, and Passengers are briefed that associated bin/compartment/closet is not used. NOTE 1: If no partitions are installed, the entire overhead stowage compartment is considered to be one bin or compartment. NOTE 2: Any emergency equipment located in the associated compartment (permanently affixed) is available for use. NOTE 3: An inoperative lid/door latch renders the lid/door inoperative. | ¦ ¦¦ ¦¦¦ ¦¦ ¦¦¦ ¦¦ ¦¦¦ ¦¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-9 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 32-01 | Galley Waste Receptacle Access Doors | C | - | - | (M)(O) May be inoperative provided: Container is empty and the access is secured to prevent waste introduction into the compartment, and Procedures are established to ensure that sufficient galley waste receptacles are available to accommodate all waste that may be generated on a flight. |  |
| 40-01 | Exterior Lavatory Door Ashtray | B | - | 0 | NOTE: Interior lavatory ashtrays considered under passenger convenience items and are not required by regulations. |  |
| 40-02 | Lavatory Waste Compartment Access Door / Flap Assembly | C | - | 0 | (M)(O) May be inoperative provided: Lavatory waste receptacle is empty, Waste compartment access is secured to prevent waste introduction, Waste compartment is placarded “INOPERATIVE – DO NOT USE”, Lavatory Smoke Detection System operates normally, and Alternate procedures are established to dispose of waste generated by lavatory use. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-10 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 40-03 | Lavatory NO SMOKING Placards |  |  |  | Must be installed and legible. NOTE: A temporary placard may be used to dispatch an aircraft to a station where normal placards are available. |  |
| 42-01 | Lavatory Door Springs | C | - | 0 | (O) May be inoperative or missing provided: Door is verified operative (open and close) without interference, Associated lavatory door is locked before each takeoff and landing, and Alternate procedures to close door(s) when required are established and used. |  |
| 51-01 | Baggage Retrieval Modules *** (600-2C10, 600-2D15, 600-2D24, 600-2E25) | D | 2 | 0 | (M) One or both may be inoperative provided affected module(s) is/are secured at the bulkhead position. | ¦ |
| 51-02 | Cargo Compartment Door Restraint Nets (Including associated equipment) | C | - | 0 | May be damaged or missing provided affected cargo compartment is empty. |  |
|  |  | C | - | 0 | (M) May be damaged or missing provided cargo in affected cargo compartment is secured. NOTE: Associated equipment includes Snap Latches, Restraint Net Brackets and Floor Pan Fitting Rings/Posts. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-11 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 51-03 | Aft Cargo Compartment Dividing Nets (Including associated equipment) *** |  |  |  |  |  |
|  | 1) 600-2B19 | D | - | 0 | May be damaged or missing provided affected cargo compartment is empty. |  |
|  |  | D | - | 0 | (M) NOTE: Associated equipment includes Quick Release Attachments, Anchor Plates, Net Posts, Narrow-Hooks and Floor Pan Fitting Rings/Posts. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | D | - | 0 | NOTE: Associated equipment includes Quick Release Attachments, Anchor Plates and Cam Buckles | ¦ |
| 51-04 | Fwd Cargo Compartment Dividing Nets (Including associated equipment) |  |  |  |  |  |
|  | 1) 600-2C10 | D | 1 | 0 | NOTE: Associated equipment includes Quick Release Attachments, Snap Latches, Anchor Plates and Floor Pan Fitting Rings/Posts. |  |
|  | 2) 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | a) Middle Nets (attached to door restrain nets) | D | 2 | 0 |  |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-12 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 51-04 | Fwd Cargo Compartment Dividing Nets (cont’d) |  |  |  |  |  |
|  | 2) 600-2D15, 600-2D24, 600-2E25 (cont’d) |  |  |  |  | ¦ |
|  | b) Divider Net (located between fwd cargo | C | 1 | 0 | May be damaged or missing provided fwd cargo compartment is empty. |  |
|  | Compartment doors) | C | 1 | 0 | May be damaged or missing provided baggage load in the fwd cargo compartment does not exceed 850 lbs. |  |
|  |  | C | 1 | 0 | (M) May be damaged or missing provided cargo in the fwd cargo compartment is secured. NOTE: Associated equipment includes Quick Release Attachments, Snap Latches, Anchor Plates and Floor Pan Fitting Rings/Posts. |  |
| 52-01 | Cargo Compartment Liners and Floor Panels | C | - | 0 | May be damaged (punctured, torn or deformed) provided the cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable). |  |
| 61-01 | Megaphones (600-2B19***, 600-2C10, 600-2D15, 600-2D24, 600-2E25) | D | - | - | (M)(O) Any in excess of those required by Regulations may be inoperative or missing provided: Inoperative megaphone is removed from the passenger cabin and its location is placarded INOPERATIVE, or it is removed from the installed location, secured out of sight and the megaphone and its installed location are placarded INOPERATIVE, Required distribution is maintained, and Procedures are established to alert crew members of an inoperative or missing megaphone. | ¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-13 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 61-01 | Megaphones (cont’d) |  |  |  |  |  |
|  |  | D | - | 0 | (O) May be inoperative provided: Aircraft crews are on the flight deck, and No passengers are carried. NOTE: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. |  |
| 61-02 | First Aid Kits | D | - | - | (O) Any kit or items contained in excess of those required by Regulations may be incomplete or missing provided: Required distribution is maintained, and Procedures are established to alert crew members of missing or incomplete kits. |  |
|  | 1) First Aid Kit Seal | A | - | - | (O) Seal affixed on the exterior of any required first aid kit may be missing or broken for three flight days provided: First Aid Kit is fully equipped or the kit has a maximum of one missing item, First Aid Kit includes a list of its contents, Inventory is taken on the content of the kit prior to departure, and Procedures are established to alert crew members of the missing or broken seal and to perform an inventory under proviso c). | ¦¦ |
| 61-03 | Fire Protection Gloves *** | D | - | 0 |  |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-14 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 61-04 | Flashlights / Flashlight Holders |  |  |  |  |  |
|  | 1) Flashlights | C | - | 0 | (O) May be inoperative or missing provided a flashlight of equivalent characteristics is readily available. |  |
|  | 2) Flashlight Holders | C | - | 0 | (M)(O) May be inoperative or missing provided alternate stowage means are provided. |  |
| 62-01 | Emergency Locator Transmitter (ELT) *** | C | - | - |  |  |
|  |  | D | - | - | Any in excess of those required by regulation may be inoperative. NOTE: Operator’s MEL must state the minimum number of ELTs required on aircraft in accordance with area of operation. |  |
| 64-01 | Flotation Equipment (Crew and Passenger) *** | C | - | - | As required by Regulations. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-15 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
| 70-01 | Passenger Convenience / NEF Items |  |  |  |  | ¦ |
|  | Passenger Convenience Items *** |  | - | 0 | Passenger convenience items, as expressed in this MMEL, are those related to passenger convenience, comfort or entertainment such as, but not limited to, galley equipment, movie equipment, ashtrays, stereo equipment, overhead reading lamps. Items addressed elsewhere in this document shall not be included. (M) and (O) procedures may be required and included in the air carrier’s appropriate document. NOTE 1: LAVATORY DOOR ASHTRAYS ARE NOT CONSIDERED CONVENIENCE ITEMS. NOTE 2: Galley equipment restraining devices such as latches, etc. must be serviceable or the compartment must not be used for storage and placarded INOPERATIVE – DO NOT USE. NOTE 3: Audio or audio-visual entertainment equipment which is used as the sole means of providing safety briefings and demonstrations is not considered a passenger convenience item. | ¦ ¦ |
|  | Non-Essential Equipment and Furnishings (NEF) *** |  | - | 0 | May be inperative, damaged or missing provided that the item(s) is deferred in accordance with the operator’s defect rectification and control procedures. The NEF policies are outlined in the operator’s Maintenance Control Manual. (M) and (O) procedures, if required, must be available to the flight crew and included in the operator’s appropriate document. NOTE: LAVATORY DOOR ASHTRAYS ARE NOT CONSIDERED CONVENIENCE ITEMS. | ¦¦¦¦¦¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 25-16 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 25 – EQUIPMENT / |  |  | 4. Remarks or Exceptions |
| FURNISHINGS |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 00-01 | FIDEEX System (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 1 | System redundancy may be degraded as indicated by “FIRE SYS FAULT” status message. NOTE: All FIDEEX System failures causing “FIRE SYS FAULT” status message must be repaired within 10 days after appearing of this message on EICAS. | ¦ |
| 00-02 | FIDEEX Control Unit ARINC Communication (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided FIRE DETECTION / FIREX MONITOR pilot initiated test is performed prior to each flight. | ¦ |
| 11-01 | Engine Fire Detection Loops |  |  |  |  |  |
|  | 1) 600-2B19 | C | 4 | 2 | One loop (A or B) may be inoperative, on each engine provided fire detection switch is selected to the operative loop. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | a) Left |  | 2 | 1 | NOTE: Item included for clarification only. Relief for single left Engine Fire Detection Loop failure is covered by item 26-00-01. |  |
|  | b) Right |  | 2 | 1 | NOTE: Item included for clarification only. Relief for single right Engine Fire Detection Loop failure is covered by item 26-00-01. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-02 | Jet Pipe Fire Detection Loops (600-2B19) | C | 4 | 2 | One loop (A or B) may be inoperative, on each engine provided fire detection switch is selected to the operative loop. |  |
| 12-01 | APU Fire Detection Loops |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | (M) One loop (A or B) may be inoperative provided APU fire detection switch is selected to the operative loop. |  |
|  |  | C | 2 | 0 | Both loops (A and B) may be inoperative provided APU is considered inoperative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 |  | 2 | 1 | NOTE: Item included for clarification only. Relief for single APU Fire Loop failure is covered by item 26-00-01. |  |
|  |  | C | 2 | 0 | Both loops (A and B) may be inoperative provided the APU is considered inoperative. |  |
|  | 3) 600-2E25 |  | 2 | 1 | NOTE: Item included for clarification only. Relief for single APU Fire Loop failure is covered by item 26-00-01. | ¦¦¦ |
|  |  | C | 2 | 0 | Both loops (A and B) may be inoperative provided: APU is considered inoperative, and Operation is limited to temperature below ISA+30. | ¦¦¦¦ |
|  | 4) 600-2C10, 600-2D15, 600-2D24 | C | 2 | 0 | (M) May be inoperative provided: APU is used on ground (for engine start only), APU access doors are opened, APU is visually monitored, APU is pneumatically loaded only, and Total APU operating time shall not exceed 5 minutes. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | APU Fire Detection Loops (cont’d) |  |  |  |  |  |
|  | 5) 600-2E25 | C | 2 | 0 | (M)(O) May be inoperative provided: APU is used on ground (for engine start only), APU access doors are opened, APU is visually monitored, APU is pneumatically loaded only, Total APU operating time shall not exceed 5 minutes, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦ ¦ ¦¦ ¦¦ |
| 12-02 | APU Fire Warning Horn (600-2B19) | C | 1 | 0 | May be inoperative provided a qualified operator remains in the cockpit to monitor the APU Fire Warning System while the APU is running. |  |
| 14-01 | Main Landing Gear Bay Overheat Detection System | B | 1 | 0 | (O) May be inoperative provided: MLG BAY OVHT warning message is not displayed, EICAS Brake Temperature Monitoring Readouts are operative, Landing gear is left extended for a minimum of ten minutes after take-off, Take-off performance is in accordance with AFM Supplement (Flight with Landing Gear Down), and Take-off is not conducted in icing conditions. NOTE: In case of engine failure after V1, performance is the prime consideration and landing gear should be retracted normally until performance penalty with gear down is not a problem. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 14-01 | Main Landing Gear Bay Overheat Detection System (cont’d) |  |  |  |  |  |
|  |  | B | 1 | 0 | (M)(O) May be inoperative provided: System is deactivated, EICAS Brake Temperature Monitoring Readouts are operative, Landing gear is left extended for a minimum of ten minutes after take-off, Take-off performance is in accordance with AFM Supplement (Flight with Landing Gear Down), and Take-off is not conducted in icing conditions. NOTE: In case of engine failure after V1, performance is the prime consideration and landing gear should be retracted normally until performance penalty with gear down is not a problem. |  |
|  |  | A | 1 | 0 | (M) May be inoperative provided: Operations are conducted in accordance with AFM Supplement (Flight with Landing Gear Down), Ground lock pins are installed to ensure that all three landing gears are locked down throughout flight, Operations are not conducted in known or forecast icing conditions, In-flight performance information given in the Flight Planning and Cruise Control Manual is used, Extended overwater operations are prohibited, Both headsets are worn, and Repairs are made within one flight day. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 15-01 | Cargo Compartment Smoke Detectors |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 0 | (M) Both may be inoperative provided cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
|  | A/c with ModSum TC601R101264 | C | 2 | 1 | (M)(O) One may be inoperative provided remaining detector is verified operative prior to each flight. |  |
|  | A/c without ModSum TC601R101264 | C | 2 | 1 | (M)(O) Forward smoke detector may be inoperative provided aft smoke detector is verified operative prior to each flight. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 (FWD CARGO) |  | 3 | 2 | NOTE: Item included for clarification only. Relief for single Fwd Cargo Compartment Smoke Detector failure is covered by item 26-00-01. | ¦ |
|  |  | C | 3 | 0 | (M) All may be inoperative provided fwd cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglss or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
|  | 3) 600-2C10, 600-2D15, 600-2D24, 600-2E25 (AFT CARGO) |  | 2 | 1 | NOTE: Item included for clarification only. Relief for single Aft Cargo Compartment Smoke Detector failure is covered by item 26-00-01. | ¦ |
|  |  | C | 2 | 0 | (M) All may be inoperative provided aft cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 16-01 | Lavatory Smoke Detection Systems | C | - | 0 | (M)(O) For each lavatory, the lavatory smoke detection system may be inoperative provided: Lavatory is not used by passengers for any purpose, Lavatory waste receptacle is empty, Lavatory door is locked CLOSED and placarded “INOPERATIVE – DO NOT ENTER”, Access to waste receptacle from outside the lavatory must be secured CLOSED and placarded “INOPERATIVE – DO NOT USE”, Lavatory is used only by aircraft crew, and In-flight service waste bags are not stored in the lavatory. NOTE 1: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. NOTE 2: The above-mentioned provisos are not intended to pleclude crew member lavatory inspections, which must be detailed in the (O) procedures. | ¦¦ ¦ ¦ ¦¦¦ ¦ ¦¦ ¦¦¦¦ |
|  |  | B | - | 0 | (O) For each lavatory, the lavatory smoke detection system may be inoperative for non-passenger carrying operations provided: Aircraft crews are the only occupants of the aircraft, and Occupants are briefed as to which smoke detection system(s) is/are inoperative, and In-flight service waste bags are not stored in the lavatory. NOTE 1: The abovementioned provisos are not intended to preclude crew member lavatory inspections which must be detailed in the (O) procedures. NOTE 2: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. | ¦¦ ¦¦¦¦ |
| Aircraft – Aéronef | Revision No – No de evision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-7 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 22-01 | APU Fire Extinguishing System |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | May be inoperative provided APU is considered inoperative. |  |
|  | 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | May be inoperative provided APU is considered inoperative. |  |
|  | 3) 600-2E25 | C | 1 | 0 | May be inoperative provided: APU is considered inoperative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦¦ |
|  | 4) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | (M) May be inoperative provided: APU is used on ground (for engine start only), APU access doors are opened, APU is visually monitored, APU Fire Detection System is operative, APU is pneumatically loaded only, and Total APU operating time shall not exceed 5 minutes. | ¦ |
|  | 5) 600-2E25 | C | 1 | 0 | (M)(O) May be inoperative provided: APU is used on ground (for engine start only), APU access doors are opened, APU is visually monitored, APU Fire Detection System is operative, APU is pneumatically loaded only, Total APU operating time shall not exceed 5 minutes, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦ ¦ ¦ ¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-8 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 23-01 | Portable Fire Extinguishers | D | - | - | (M)(O) Any in excess of those required by Regulations may be inoperative or missing provided: Inoperative fire extinguisher is removed from the passenger cabin or flight compartment and its location is placarded INOPERATIVE, or it is removed from the installed location, secured out of sight and the fire extinguisher and its installed location are placarded INOPERATIVE, Required distribution is maintained, and Procedures are established to alert crew members of missing or inoperative fire extinguishers. |  |
| 25-01 | Cargo Compartment Fire Extinguishing System |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | May be inoperative provided cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | May be inoperative provided both cargo compartments are empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) | ¦ |
| 25-02 | Cargo Compartment Fire Extinguisher Squibs |  |  |  |  |  |
|  | 1) 600-2B19 | A | 4 | 3 | One may be inoperative provided: Cargo fire test is performed before each departure, and Repairs are made within three flight days. |  |
|  |  | C | 4 | 0 | All may be inoperative provided cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
|  |  |  |  |  | cont’d |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-9 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 25-02 | Cargo Compartment Fire Extinguisher Squibs (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | a) Fwd squibs | C | 2 | 0 | All may be inoperative provided fwd cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
|  | b) Aft squibs | C | 2 | 0 | All may be inoperative provided aft cargo compartment is empty. (For ballast purposes, use of bags (made of fiberglass or kevlar) of sand or ingots of non-magnetic metals (such as lead) is acceptable) |  |
| 26-01 | Lavatory Fire Extinguishing Systems | C | - | 0 | (M)(O) May be inoperative provided lavatory Smoke Detection System operates normally. |  |
|  |  | C | - | 0 | (M)(O) May be inoperative provided: Lavatory is not used by passengers for any purpose, Lavatory waste receptacle is empty, Lavatory door is locked CLOSED and placarded “INOPERATIVE DO NOT ENTER”, Access to waste receptacle from outside the lavatory must be secured CLOSED and placarded “INOPERATIVE – DO NOT USE”, and Lavatory is used only by aircraft crew. NOTE: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. | ¦¦¦¦ |
|  |  |  |  |  | cont’d |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 26-10 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 26 – FIRE PROTECTION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 26-01 | Lavatory Fire Extinguishing Systems (cont’d) |  |  |  |  |  |
|  |  | B | - | 0 | (O) May be inoperative for non-passenger carrying operations provided: Aircraft crews are the only occupants of the aircraft, and Occupants are briefed as to which lavatory fire extinguishing system(s) is/are inoperative. NOTE 1: The abovementioned provisos are not intended to preclude crew member lavatory inspections which must be detailed in the (O) procedures. NOTE 2: For the purpose of this item “aircraft crew” is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. | ¦ |

| Aircraft – Aéronef | Revision No – No de evision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 00-01 | PULL & TURN Placards | C | 2 | 0 | May be illegible or missing provided a readily visible label stating PULL & TURN is installed. |  |
| 12-01 | Aileron Trim System |  |  |  |  |  |
|  | 1) 600-2B19 | B | 1 | 0 | May be inoperative provided: Autopilot is operative, Both Power Crossflow SOVs are operative, and Aileron trim system is centered. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 1 | 0 | May be inoperative provided: Autopilot is operative, X-Flow Pump is operative, and Aileron trim system is centered. | ¦ |
| 15-01 | EICAS LH and RH Aileron Control Surface Position Indication | C | 1 | 0 | (M) May be inoperative provided visual inspection of affected control surface for correct operation is made before each departure. |  |
| 15-02 | Aileron Flutter Dampers | A | 2 | 2 | (O) One per surface may indicate low reservoir fluid provided: Each individual PCU is verified operative prior to further flight, and Repairs are made within one flight day. |  |
| 21-01 | Rudder System (600-2E25) | C | 1 | 1 | System redundancy may be degraded as indicated by RUDDER FAULT status message provided that one of the following indications or messages is also present: Rad Alt red flag, or IAPS DEGRADED status message, or FLAP HALFSPEED status message, or SLAT HALFSPEED status message, or L FADEC FAULT 1(2) status message, or R FADEC FAULT 1(2) status message, A/SKID INBD caution message, or A/SKID OUTBD caution message. | ¦¦¦ ¦¦ ¦ ¦ ¦ ¦ ¦ ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-01 | EICAS Rudder Control Surface Position Indication (600-2B19) | C | 1 | 0 | (M) May be inoperative provided visual inspection of affected control surface for correct operation is made before each departure. |  |
| 24-02 | Rudder Pedal Adjustment Systems | C | 2 | 1 | (O) One may be inoperative provided: Pedals are in position acceptable to affected crewmember, EICAS Rudder Control Surface Position Indication is operative, and Rudder and brake pedals are checked for full and unrestricted movement at both pilot stations. |  |
| 34-01 | EICAS Elevator Control Surface Position Indication (600-2B19) | C | 1 | 0 | (M) May be inoperative provided visual inspection of affected control surface for correct operation is made before each departure. |  |
| 35-01 | Stall Warning Switch Lights (light function only) | C | 2 | 1 | (O) One may be inoperative provided shaker and pusher are checked operative prior to each flight. |  |
| 51-01 | Flap Electronic Control Unit (FECU) Channels (600-2B19) |  |  |  |  |  |
|  | 1) A/c without ModSum TC601R15447 or TC601R15318 | C | 2 | 1 | May be inoperative provided Flap Power Drive Unit Motor on the opposite side is operative. NOTE: Flap will operate at half speed. |  |
|  | Flap Power Drive Unit (PDU) Motors | B | 2 | 1 | NOTE: Flap will operate at half speed. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Flap Electronic Control Unit (FECU) Channels (600-2B19) (cont’d) |  |  |  |  |  |
|  | 2) A/c with ModSum TC601R15447 or TC601R15318 | C | 2 | 1 | May be inoperative provided: Flap Power Drive Unit Motor on the opposite side is operative, and Skew Detection System is considered inoperative. NOTE: Flap will operate at half speed. |  |
|  |  | C | 2 | 1 | (M) May be inoperative provided: Flap Power Drive Unit Motor on the opposite side is operative, and Skew Detection System is verified operative before each flight. NOTE: Flap will operate at half speed. |  |
|  | Flap Power Drive Unit (PDU) Motors | B | 2 | 1 | May be inoperative provided Skew Detection System is considered inoperative. NOTE: Flap will operate at half speed. |  |
|  |  | B | 2 | 1 | (M) May be inoperative provided Skew Detection System is verified operative before each flight. NOTE: Flap will operate at half speed. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | Slat / Flap System |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24 without ModSum 670T31732) |  |  |  |  |  |
|  | Flap Subsystem | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “FLAPS HALFSPEED” status message provided: Both Flap PDU brakes are verified operative, “SLATS HALFSPEED” status message is not displayed, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). NOTE: Flaps will operate at half speed. |  |
|  | Slat Subsystem | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “SLATS HALFSPEED” status message provided: Both Slat PDU brakes are verified operative, “FLAPS HALFSPEED” status message is not displayed, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). NOTE: Slats will operate at half speed. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | Slat / Flap System (cont’d) |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24 with ModSum 670T31732), (600-2E25) |  |  |  |  | ¦ |
|  | Flap Subsystem | C | 1 | 1 | System redundancy may be degraded as indicated by “FLAPS HALFSPEED” status message provided: “SLATS HALFSPEED” and “FLAP FAULT” status messages are not displayed, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). NOTE: Flaps will operate at half speed. |  |
|  | Slat Subsystem | C | 1 | 1 | System redundancy may be degraded as indicated by “SLATS HALFSPEED” status message provided: “FLAPS HALFSPEED” and “FLAP FAULT” status messages are not displayed, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). NOTE: Slats will operate at half speed. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-03 | Skew Detection System (600-2B19 with ModSum TC601R15447 or TC601R15318) | C | 1 | 0 | (M)(O) May be inoperative provided: System is deactivated, and Flaps are visually checked before each flight. |  |
|  |  | B | 1 | 0 | (M)(O) May be inoperative provided: System reset is performed before each flight, Flaps are visually checked before each flight, and EICAS “FLAPS FAIL” caution message is not displayed. NOTE1: On the aircraft without ModSum TC601R15059 or TC601R15010 (Non EICAS 2000) flap will operate at half speed. NOTE2: On the aircraft with ModSum TC601R15059 or TC601R15010 (EICAS 2000) flap may operate at half speed if the Skew Detection System DC power supply fails. |  |
| 51-04 | Slat Disconnect Detection System |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24 without ModSum 670T30446) | A | 1 | 0 | (M) May be inoperative as indicated by “SLAT FAULT” status message provided: Slats are inspected once each flight day to ensure no mechanical disconnect is present, and Repairs are made within three flight days. | ¦¦¦¦¦ |
|  | (600-2C10, 600-2D15, 600-2D24 with ModSum 670T30446) | A | 1 | 0 | (M)(O) May be inoperative as indicated by “SLAT FAULT” status message provided: Slats are inspected once each flight day to ensure no mechanical disconnect is present, Slats are inspected before next flight to ensure no mechanical disconnect is present if 0g or negative g is encountered as result of pilot maneuvering in last flight, and Repairs are made within three flight days. | ¦ ¦ ¦ ¦ ¦¦¦¦ ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-05 | Flap System |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24 without ModSum 670T31732) | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “FLAP FAULT” status message provided non-dispatchable Flap System failures are verified not present before each flight. |  |
|  | (600-2C10, 600-2D15, 600-2D24 with ModSum 670T31732), (600-2E25) | C | 1 | 1 | System redundancy may be degraded as indicated by “FLAP FAULT” status message. | ¦ |
| 54-01 | Flap Position Potentiometers (600-2B19) |  |  |  |  |  |
|  | 1) A/c without ModSum TC601R15447 or TC601R15318 | C | 2 | 1 | (M) May be inoperative provided affected potentiometer is deactivated. |  |
|  | 2) A/c with ModSum TC601R15447 or TC601R15318 |  |  |  |  |  |
|  | a) L/H | C | 1 | 0 | (M) May be inoperative provided: Affected potentiometer is deactivated, R/H Flap Position Potentiometer is operative, and Skew Detection System is considered inoperative. |  |
|  | b) R/H | C | 1 | 0 | (M) May be inoperative provided: Affected potentiometer is deactivated, and L/H Flap Position Potentiometer is operative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-8 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 60-01 | EICAS Ground Spoilers Control Surface Position Indications | C | 4 | 0 | (M) Any may be inoperative provided: GLD auto and manual modes are visually verified operative prior to each flight, and GLD spoilers are verified stowed prior to each flight. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-9 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 62-01 | Spoiler Electronic Control Unit (SECU) Channels (600-2B19) |  |  |  |  |  |
|  | 1) Flight Spoiler Channels | B | 2 | 1 | (M)(O) One may be inoperative provided: INBD and OUTBD Ground Spoilers are verified operative prior to each flight, Flight spoilers are verified operative prior to each flight, EICAS "R/L FLIGHT SPOILER", "FLIGHT SPOILERS" and FLIGHT SPOILER DEPLOY" caution messages are not displayed, and T/O Configuration Warning System is verified operative before first flight each day. |  |
|  | 2) Ground Spoiler Channels | B | 4 | 2 | (O) One per SECU may be inoperative provided: INBD and OUTBD Ground Spoilers are verified operative prior to each flight, and T/O Configuration Warning System is verified operative before first flight each day. |  |
|  | 3) Spoileron Channels | A | 2 | 1 | (M)(O) One may be inoperative provided: Spoilerons are verified operative prior to each flight, Remaining SECU Spoileron Channel is controlled by SECU p/n 49-164-05, 49-164-07 or 49-164-21, EICAS "SPOILERONS ROLL", "SPOILERONS" and "R/L SPOILERON" caution messages are not displayed, T/O Configuration Warning System is verified operative before first flight each day, and Repairs are made within three flight days. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-10 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 62-02 | Flight Spoiler PCUs (600-2B19) | B | 4 | 2 | (M)(O) One Flight Spoiler PCU per surface may be inoperative provided: INBD and OUTBD Ground Spoilers are confirmed operative prior to each flight, Flight spoilers are confirmed operative prior to each flight, Both SECU Channels are operative, EICAS "R/L FLIGHT SPOILER", "FLIGHT SPOILERS" and "FLIGHT SPOILER DEPLOY" caution messages are not displayed, and T/O Configuration Warning System is verified operative before first flight each day. |  |
| 62-03 | Spoileron PCUs (600-2B19) | A | 4 | 2 | (M)(O) One per surface may be inoperative provided: Spoilerons are verified operative prior to each flight, One spoileron PCU per surface is controlled by SECU p/n 49-164-05, 49-164-07 or 49-164-21, EICAS "SPOILERONS ROLL", "SPOILERONS" and "R/L SPOILERON" caution messages are not displayed, T/O Configuration Warning System is verified operative before first flight each day, and Repairs are made within three flight days. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-11 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 65-01 | Ground Spoilers (Inboard or Outboard Pair) (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | (M)(O) One pair of Ground Spoilers Inboard (IB) or Outboard (OB) may be inoperative in the RETRACTED position provided: All remaining spoiler surfaces are operative in GLD auto and manual modes, Affected inboard or outboard Ground Spoiler pair is secured stowed, Both surfaces of the inoperative pair are verified fully retracted prior to each flight, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 2 | 1 | (M)(O) One pair of Ground Spoilers Inboard (IB) or Outboard (OB) may be inoperative in the RETRACTED position provided: All MFS and the remaining ground spoiler pair is operative in GLD AUTO and Manual ARM modes, Affected inboard or outboard Ground Spoiler pair is secured stowed, Both surfaces of the inoperative pair are verified fully retracted prior to the each flight, Both Thrust Reversers are operative, No other GS, MFS status message are displayed, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 27-12 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 27 – FLIGHT CONTROLS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 65-02 | Spoiler and Stabilizer Control System (SSCS) |  |  |  |  |  |
|  | 1) SSCU 1 Channels (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | May be inoperative as indicated by “SSCU 1 FAULT” status message provided both SSCU 2 Channels are operative. | ¦ |
|  | 2) SSCU 2 Channels (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | May be inoperative as indicated by “SSCU 2 FAULT” status message provided both SSCU 1 Channels are operative. | ¦ |
|  | 3) Spoiler / Stabilizer Subsystem |  |  |  |  |  |
|  | a) (600-2C10, 600-2D15, 600-2D24 without ModSum 670T31194) | C | 1 | 1 | (M) System redundancy may be degraded as indicated by “SPLR/STAB FAULT” status message provided: Both SSCU 1 Channels and both SSCU 2 Channels are operative, and Not-dispatchable spoiler / stabilizer subsystem failures are verified not present once each flight day. |  |
|  | b) (600-2C10, 600-2D15, 600-2D24 with ModSum 670T31194), (600-2E25) | C | 1 | 1 | System redundancy may be degraded as indicated by “SPLR/STAB FAULT” status message provided both SSCU 1 Channels and both SSCU 2 Channels are operative. | ¦ |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 13-01 | APU Fuel Feed SOV |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M) May be inoperative CLOSED provided APU is considered inoperative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | (M) May be inoperative CLOSED provided APU is considered inoperative. |  |
|  |  | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: APU is used for engine starting on ground only, APU is shutdown after one engine start, APU is not used in flight, APU Fire Detection System is operative, and APU Fire Extinguishing System is operative. |  |
|  | 3) 600-2E25 | C | 1 | 0 | (M) May be inoperative CLOSED provided: APU is considered inoperative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦¦ |
|  |  | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: APU is used for engine starting on ground only, APU is shutdown after one engine start, APU is not used in flight, APU Fire Detection System is operative, APU Fire Extinguishing System is operative, and Operation is limited to temperature below ISA+30. | ¦ ¦¦ ¦ ¦ ¦ ¦¦ ¦¦ |
| 13-02 | XFLOW AUTO OVERRIDE "MAN" Switch Light (light function only) | C | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-2 ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 13-03 | XFLOW L/R "ON/FAIL" Switch Lights (light function only) | C | 2 | 0 |  |  |
| 13-04 | GRAVITY XFLOW “OPEN/FAIL” Switch Light (light function only) | C | 1 | 0 |  |  |
| 13-06 | Power Crossflow SOVs (600-2B19) | C | 2 | 0 | (O) May be inoperative CLOSED provided: All Fuel Quantity Readouts are operative, and Gravity crossflow SOV is verified operative before each flight. |  |
| 13-07 | Transfer Ejectors (Center Tank) |  |  |  |  |  |
|  | 1) 600-2B19 | B | 2 | 1 | (M) One may be inoperative provided: Center tank is empty, and EICAS Center Tank Fuel Quantity Readout is operative. |  |
|  |  | B | 2 | 1 | (M) One may be inoperative provided: Center tank contains less than 500 pounds of fuel at dispatch, Remaining fuel in center tank is considered unusable, Aircraft range is limited accordingly, EICAS Center Tank Fuel Quantity Readout is operative, Both Power Crossflow SOVs are operative, and XFLOW/APU Fuel Pump is operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-3 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 13-07 | Transfer Ejectors (Center Tank) (cont’d) |  |  |  |  |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 2 | 1 | (M) One may be inoperative provided: Center tank is empty, and EICAS Center Tank Fuel Quantity Readout is operative. | ¦ |
|  |  | B | 2 | 1 | (M) One may be inoperative provided: Center tank contains less than 500 pounds of fuel at dispatch, Fuel imbalance between wing tanks is less than 300 lbs at dispatch, Remaining fuel in center tank is considered unusable, Aircraft range is limited accordingly, EICAS Center Tank Fuel Quantity Readout is operative, and Flight crew monitors center tank fuel quantity for proper transfer. |  |
| 13-08 | Fuel Transfer SOVs (Center Tank) |  |  |  |  |  |
|  | 1) 600-2B19 | B | 2 | 1 | (M) One may be inoperative CLOSED provided: Center tank is empty, Opposite Transfer Ejector (Center Tank) is operative, and EICAS Center Tank Fuel Quantity Readout is operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 13-08 | Fuel Transfer SOVs (Center Tank) (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (cont’d) | B | 2 | 1 | (M) One may be inoperative CLOSED provided: Center tank contains less than 500 pounds of fuel at dispatch, Opposite Transfer Ejector (Center Tank) is operative, Remaining fuel in center tank is considered unusable, Aircraft range is limited accordingly, EICAS Center Tank Fuel Quantity Readout is operative, Both Power Crossflow SOVs are operative, and XFLOW/APU Fuel Pump is operative. |  |
|  | Without ModSum TC601R12716 | C | 2 | 0 | (M) Both may be inoperative OPEN provided center tank is empty. |  |
|  | With ModSum TC601R12716 | C | 2 | 0 | (M) Both may be inoperative OPEN. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 2 | 1 | (M) One may be inoperative CLOSED provided: Center Tank is empty, Opposite Transfer Ejector (Center Tank) is operative, and EICAS Center Tank Fuel Quantity Readout is operative. | ¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-5 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 13-08 | Fuel Transfer SOVs (Center Tank) (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 (cont’d) | B | 2 | 1 | (M) One may be inoperative CLOSED provided: Center tank contains less than 500 pounds of fuel at dispatch, Opposite Transfer Ejector (Center Tank) is operative, Fuel imbalance between wing tanks is less than 300 lbs at dispatch, Remaining fuel in center tank is considered unusable, Aircraft range is limited accordingly, EICAS Center Tank Fuel Quantity Readout is operative, and Flight crew monitors center tank fuel quantity for proper transfer. |  |
|  |  | C | 2 | 0 | (M) Both may be inoperative OPEN provided center tank is empty. |  |
| 13-10 | XFlow Pump (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M)(O) May be inoperative provided: All EICAS Fuel Tank Quantity Readouts are operative, and Gravity crossflow SOV is verified operative. | ¦ |
| 23-01 | Fuel Boost Pumps |  |  |  |  |  |
|  | 600-2B19 | B | 2 | 1 | (M) One may be inoperative provided: Inoperative boost pump is selected OFF, Inoperative boost pump is deactivated, XFLOW/APU Fuel Pump is operative, and Power Crossflow SOVs are operative. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 2 | 1 | (M) One may be inoperative provided: Inoperative boost pump is deactivated, and XFlow Pump is operative. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-6 ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 23-02 | Fuel Boost Pumps “ON/INOP” Switch Lights (light function only) | C | 2 | 0 |  |  |
| 24-01 | XFLOW/APU Fuel Pump (600-2B19) | C | 1 | 0 | (M) May be inoperative provided: APU is considered inoperative, Power Crossflow SOVs are considered inoperative, All Fuel Quantity Readouts are operative, and Operations are conducted in accordance with AFM if fuel crossflow is required. |  |
|  |  | C | 1 | 0 | (M)(O) May be inoperative provided: Satisfactory APU operations with both engines OFF is established before each departure by starting the APU using Fuel Boost Pumps, selecting APU Bleed ON, selecting both Air Conditioning Packs ON, and verifying the APU operates normally, Power Crossflow SOVs are considered inoperative, All Fuel Quantity Readouts are operative, Operations are conducted in accordance with AFM if fuel crossflow is required, APU Battery is operative, and APU Battery Charger is operative. NOTE: Auto and Manual power crossflow are inoperative for either option. |  |
| 24-02 | APU Negative Gravity Feed Check Valve (600-2B19) | C | 1 | 0 | (O) May be inoperative provided flight operations are not dependent on use of the APU. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-03 | APU Fuel Pump (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative provided APU is considered inoperative. | ¦ |
| 24-04 | APU PWR FUEL "PUMP FAIL / SOV FAIL" Switch Lights (light function only) | C | 1 | 0 |  |  |
| 25-01 | External Single Point Pressure Refueling System (Refuel/Defuel Control Panel) | C | 1 | 0 | May be inoperative provided Internal Single Point Pressure Refueling System is operative. |  |
|  | (600-2B19) | C | 1 | 0 | (O) May be inoperative provided gravity refueling procedures are used. Refer to AFM for reduced fuel quantity available when using gravity refueling. |  |
|  | Automatic Mode | C | 1 | 0 | (O) May be inoperative provided manual or gravity refueling procedure is used. |  |
|  | Manual Mode | C | 1 | 0 | (O) May be inoperative provided automatic or gravity refueling procedure is used. |  |
|  | Fuel Quantity Display Indication | C | 1 | 0 | (O) May be inoperative provided: Manual or gravity refueling procedure is used, and All EICAS Fuel Tank Quantity Readouts are operative. |  |
|  |  | C | 1 | 0 | (O) May be inoperative provided: Manual or gravity refueling procedure is used, and All MLIs are operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-8 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 25-01 | External Single Point Pressure Refueling System (Refuel/Defuel Control Panel) (cont’d) |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided gravity refueling procedures are used. Refer to AFM for reduced fuel quantity available when using gravity refueling. | ¦ |
|  | Automatic Mode | C | 1 | 0 | May be inoperative provided manual or gravity refueling procedure is used. |  |
|  | Manual Mode | C | 1 | 0 | May be inoperative provided automatic or gravity refueling procedure is used. |  |
|  | Fuel Quantity Display Indication | C | 1 | 0 | May be inoperative provided: Manual or gravity refueling procedure is used, and All EICAS Fuel Tank Quantity Readouts are operative. |  |
|  |  | C | 1 | 0 | May be inoperative provided: Manual or gravity refueling procedure is used, and All MLIs are operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-9 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 25-02 | Refuel/Defuel Adapter Cap | C | 1 | 0 | (M) May be inoperative (missing) provided: Pressure-refueling adapter door is not missing, Refuel/defuel adapter is visually checked for contamination prior to each refueling, and No leakage can be detected after refueling is complete. |  |
| 25-03 | Refuel SOVs |  |  |  |  |  |
|  | 1) 600-2B19 | C | 3 | 0 | (M) May be inoperative CLOSED provided gravity refueling procedures are used. NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. |  |
|  | 2) Wing (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 0 | (M) May be inoperative CLOSED provided gravity refueling procedures are used for the affected tank(s). NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. | ¦ |
|  | 3) Center (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided center tank remains empty once remaining fuel is consumed. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-10 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 25-04 | High Level Sensors |  |  |  |  |  |
|  | 1) 600-2B19 | C | 3 | 0 | May be inoperative provided gravity refueling procedures are used for affected tank. NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. |  |
|  | 2) Wing (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 0 | (O) Both may be inoperative provided: Gravity refueling procedures are used for affected wing tank, All EICAS Fuel Tank Quantity Readouts are operative, XFlow Pump is operative, Both Transfer Ejectors are operative, and Both Transfer SOVs are operative. NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. | ¦ |
|  | 3) Center (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided center tank remains empty. | ¦ |
| 25-05 | Internal Single Point Pressure Refueling System (Refuel/Defuel Control Panel) *** | D | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-11 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | EICAS Bulk Fuel Temperature Indication | C | 1 | 0 | (O) May be inoperative provided: TAT is used as an indication of fuel temperature, TAT is monitored during flight, For the first Flight of the day, the ambient overnight temperatures were above -29°C for A/C last fuelled with Jet A or above -36°C for A/C last fuelled with Jet A-1, and On subsequent Flights, when refueling activities are to be conducted, local temperatures are to be above -25°C for A/C using Jet A or above -32 for A/C using Jet A-1 for at least 10 hours prior to the re-fuelling. | ¦ ¦¦¦¦ ¦¦¦¦¦ |
| 41-01 | EICAS Fuel Tank Quantity Readouts (Left, Right and Total) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 3 | 1 | (M)(O) One main tank quantity readout plus total quantity readout may be inoperative provided: Both LH and RH tanks are completely filled, XFLOW auto-override is selected to MANUAL, and Aircraft is refueled using Single Point Pressure Refueling System. |  |
|  |  | C | 3 | 1 | (M)(O) One main tank quantity readout plus total quantity readout may be inoperative provided: Total fuel carried includes at least 10% more than the fuel load required for the planned flight and this extra fuel is considered unusable, Manual or gravity refueling mode is used, MLIs are used to verify main tank quantities prior to each flight, and XFLOW auto-override is selected to MANUAL. NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. CAUTION: Ensure FCOM MLI Chart, LBS or KG column, is used as applicable. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-12 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-01 | EICAS Fuel Tank Quantity Readouts (Left, Right and Total) (cont’d) |  |  |  |  |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 3 | 1 | (M)(O) One main fuel tank quantity readout plus total quantity readout may be inoperative provided: Both LH and RH tanks are completely filled, XFLOW auto-override is selected to MANUAL, Airplane is refueled using Single Point Pressure Refueling System, Associated High Level Sensor is operative, Opposite side Transfer Ejector is operative, and Opposite side Fuel Transfer SOV is operative. | ¦ |
|  |  | B | 3 | 1 | (M)(O) One main fuel tank quantity readout plus total quantity readout may be inoperative provided: Total fuel carried includes at least 15% more than the fuel load required for the planned flight, Manual or gravity refueling mode is used, MLIs are used to verify main tank quantities before each flight, XFLOW auto-override is selected to MANUAL, Associated High Level Sensor is operative, Opposite side Transfer Ejector is operative, and Opposite side Fuel Transfer SOV is operative. NOTE: Refer to AFM for reduced fuel quantity available when using gravity refueling. CAUTION: Ensure FCOM MLI Chart, LBS or KG column, is used as applicable. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-13 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-02 | EICAS Fuel Tank Quantity Readouts (Center and Total) |  |  |  |  |  |
|  | 600-2B19 | C | 2 | 0 | (M) Both may be inoperative provided: Center tank remains empty, Left and Right EICAS Fuel Tank Quantity Readouts are operative, and MLI is used to verify that center tank is empty once each flight day, |  |
|  |  | C | 2 | 0 | (M) Both may be inoperative provided: Center tank is completely filled, Left and Right EICAS Fuel Tank Quantity Readouts are operative, and Aircraft is refueled using Single Point Pressure Refueling System. |  |
|  |  | C | 2 | 0 | (M) Both may be inoperative provided: Center tank is refueled using Single Point Pressure Refueling System, MLI is used to verify center tank quantity prior to each flight, and Left and Right EICAS Fuel Tank Quantity Readouts are operative. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 2 | 0 | (M)(O) Both may be inoperative provided: Center fuel tank remains empty, Left and Right EICAS Fuel Tank Quantity Readouts are operative, and MLI is used to verify that center tank is empty once each flight day. | ¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-14 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-02 | EICAS Fuel Tank Quantity Readouts (Center and Total) (cont’d) |  |  |  |  |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 (cont’d) | B | 2 | 0 | (M)(O) Both may be inoperative provided: Center fuel tank is completely filled, Left and Right EICAS Fuel Tank Quantity Readouts are operative, and Aircraft is refueled using Single Point Pressure Refueling System. | ¦ |
|  |  | B | 2 | 0 | (M)(O) Both may be inoperative provided: Center fuel tank is refueled using Single Point Pressure Refueling System, MLI is used to verify center tank quantity before each flight, and Left and Right EICAS Fuel Tank Quantity Readouts are operative. |  |
| 41-03 | Fuel Computer Channels |  |  |  |  |  |
|  | 1) 600-2B19 (FSC) | B | 2 | 1 | One may be inoperative provided: Both Transfer Ejectors (Center Tank) are operative, Both Fuel Transfer SOVs (Center Tank) are operative, Both Fuel Flow "FF" Readouts are operative, and Fuel Used Readout on synoptic page is operative and reset prior to each flight. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 (FQGC) | B | 2 | 1 | (O) One may be inoperative provided: Remaining fuel in center tank is considered unusable, Center tank contains less than 500 pounds of fuel at dispatch, and Gravity crossflow SOV is verified operative. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-15 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-04 | Magnetic Level Indicators | C | 5 | 0 | All may be inoperative provided associated EICAS Fuel Tank Quantity Readouts are operative. |  |
| 41-05 | Fuel Pitch and Roll Inclinometers | C | 2 | 0 | May be inoperative provided all EICAS Fuel Tank Quantity Readouts (Left, Right, Center and Total) are operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 28-16 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 28 – FUEL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Engine Driven Pumps (EDP) (Systems 1 and 2) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | (M)(O) One may be inoperative provided: Hydraulic AC Motor Pump (ACMP) 1B and Hydraulic AC Motor Pump (ACMP) 2B are operated continuously during flight, All Hydraulic AC Motor Pumps (ACMP) are operative, Affected pump is mechanically removed and a blanking plate is installed, Both Integrated Drive Generators (IDG) are operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 2 | 1 | (M)(O) One may be inoperative provided: Same side Hydraulic AC Motor Pump (ACMP) is operated continuously during flight, All Hydraulic AC Motor Pumps (ACMP) are operative, Affected pump is mechanically removed and a blanking plate is installed, Flexible hydraulic lines at the pylon quick-disconnects are disconnected, capped and stowed, and Repairs are made within one flight day. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-02 | Hydraulic AC Motor Pumps (ACMP) (Systems 1 and 2) (600-2B19) |  |  |  |  |  |
|  | a) ACMP 1B | C | 1 | 0 | (M) May be inoperative provided: All other hydraulic pumps are operative, Affected pump is selected OFF, Inboard Ground Spoiler Pair is operative, Nosewheel Steering is operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | b) ACMP 2B | C | 1 | 0 | (M) One may be inoperative provided: All other hydraulic pumps are operative, Affected pump is selected OFF, Outboard Ground Spoiler Pair is operative, Nosewheel Steering is operative, Both Thrust Reverser Systems are operative, Inboard Anti-Skid (System) Channel is operative, Take-off or landing is not conducted from a contaminated runway, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
| 11-03 | Hydraulic Heat Exchanger Cooling Fan | C | 1 | 0 | May be inoperative provided hydraulic temperature of #1 and #2 systems on the synoptic page is monitored not to exceed 96 degrees C during ground operations. |  |
| 11-04 | Hydraulic Switches "AUTO" Function (Hydraulic AC Motor Pumps) | C | 3 | 0 | All may be inoperative provided affected Pumps are manually selected ON before each take-off and landing. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-05 | Hydraulic Accumulator Pressure Gauges (Systems 1, 2 and 3) | C | 3 | 0 | (M) All may be inoperative provided accumulator pre-charge pressure is checked using a suitable ground gauge. |  |
| 11-06 | Hydraulic Accumulators (Systems 1 and 2) | B | 2 | 0 |  |  |
| 11-07 | Return Manifold Filter – Differential Pressure Indicators | A | 3 | 0 | (M) All may be inoperative provided: Filter element is verified free of any metal contaminant, and Repairs are made within one flight day. |  |
| 11-08 | Hydraulic Firewall SOVs (Systems 1 and 2) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 2 | 1 | (M) May be inoperative provided: Affected hydraulic firewall SOV is deactivated, Flexible hydraulic lines at the pylon quick-disconnects are disconnected, capped and stowed, Same side Engine Driven Pump (EDP) is considered inoperative, and Engine Driven Pump (EDP) on the opposite side is operative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 2 | 1 | (M) May be inoperative provided: Affected hydraulic firewall SOV is deactivated, Same side Engine Driven Pump (EDP) is considered inoperative, Engine Driven Pump (EDP) on the opposite side is operative, and Repairs are made within one flight day. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | Hydraulic AC Motor Pump (ACMP) 3A |  |  |  |  |  |
|  | 1) 600-2B19 | B | 1 | 0 | (M)(O) May be inoperative provided: Hydraulic AC Motor Pumps (ACMP) 3B is operated continuously during flight, Both Integrated Drive Generators (IDG 1 and IDG 2) are operative, All other hydraulic pumps are operative, and Takeoff and landing performance is in accordance with the AFM Supplement (Flight with Landing Gear Down). |  |
|  | 2) 600-2C10 | A | 1 | 0 | (M)(O) May be inoperative provided: Hydraulic AC Motor Pumps (ACMP) 3B is operated continuously during flight, All other hydraulic pumps are operative, and Repairs are made within one flight day. |  |
|  | 3) 600-2D15, 600-2D24, 600-2E25 | A | 1 | 0 | (M)(O) May be inoperative provided: Hydraulic AC Motor Pumps (ACMP) 3B is operated continuously during flight, All other hydraulic pumps are operative, Cat II and Cat III A operations are prohibited, Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative), and Repairs are made within one flight day, | ¦ ¦¦¦ ¦ |
| 31-01 | EICAS Hydraulic Pressure Readouts (Systems 1, 2 and 3) (600-2B19, 600-2C10, 600-2D15, 600-2D24) | C | 3 | 0 | (O) All may be inoperative provided associated pressure switches are operative. | ¦¦¦¦ |
| 32-01 | EICAS Hydraulic Reservoir Quantity Readouts (Systems 1, 2 and 3) | C | 3 | 0 | (O) All may be inoperative provided quantity in associated reservoir(s) is checked on the reservoir sight glass before each departure. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-5 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 34-01 | Hydraulic Pump Low Pressure Switches (Systems 1, 2 and 3) | C | 6 | 3 | (O) Three may be inoperative provided: At least one Low Pressure Switch is operative for each hydraulic system, and Associated Hydraulic Pressure and Quantity Readouts are monitored during flight. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 29-6 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 29 – HYDRAULIC POWER |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 12-01 | Wing Anti-Ice Modulating and SOVs (Wing Anti-Ice Valve) | C | 2 | 0 | (M) Both may be inoperative provided: Valves are secured CLOSED, Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. |  |
|  | 1) 600-2B19 | C | 2 | 1 | (M) May be inoperative CLOSED provided: Valve is secured CLOSED, and 14th Stage ISOL Valve is operative and selected OPEN. |  |
|  | 2) (600-2C10, 600-2D15, 600-2D24 without ModSum 670T11216) | C | 2 | 1 | (M)(O) May be inoperative CLOSED provided: Air Conditioning Pack on the affected side is operative and is operated continuously throughout flight, Wing Cross Bleed Valve is operative, Wing cross bleed selector switch is selected to the opposite side (FROM LEFT or FROM RIGHT), and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 3) (600-2C10, 600-2D15, 600-2D24 with ModSum 670T11216), (600-2E25) | C | 2 | 1 | (M) May be inoperative CLOSED provided: Wing Cross Bleed Valve is operative, Wing cross bleed selector switch is selected to the opposite side (FROM LEFT or FROM RIGHT), and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 12-02 | 14th Stage ISOL Valve (600-2B19) | C | 1 | 0 | (M) May be inoperative OPEN provided: Valve position indication is operative, Both Ice Detection Systems are operative, Both 14th Stage SOVs are operative, and Both Wing Anti-Ice Modulating and SOVs are operative. |  |
| 12-03 | Wing Anti-Ice System (600-2B19) | C | 1 | 0 | May be inoperative provided: Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. |  |
|  | 1) Normal Control | C | 1 | 0 | (M)(O) May be inoperative provided: Standby Control is verified operative prior to each flight, Both Ice Detection Systems are operative, and 14th Stage Isolation Valve is operative. |  |
|  | 2) Standby Control | C | 1 | 0 | (M) May be inoperative provided Normal Control is operative. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-3 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 12-04 | Wing Anti-Ice Temperature Sensor Elements |  |  |  |  |  |
|  | 1) Inboard/ Outboard (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 8 | 0 | May be inoperative provided: Wing Anti-Ice System is selected OFF, Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. NOTE: Caution message(s) will revert to a status “WING A/I FAULT” upon selection of wing anti-ice system to OFF. | ¦ |
|  | 2) Inboard |  |  |  |  |  |
|  | (600-2C10, 600-2D15, 600-2D24 without ModSum 670T11216) | C | 4 | 2 | (O) Two elements in one sensor pair may be inoperative provided: Air Conditioning Pack on the affected side is operative and is operated continuously throughout flight, Wing Cross Bleed Valve is operative, Wing cross bleed selector switch is selected to the opposite side (FROM LEFT or FROM RIGHT), and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | (600-2C10, 600-2D15, 600-2D24 with ModSum 670T11216), (600-2E25) | C | 4 | 2 | (O) Two elements in one sensor pair may be inoperative provided: Wing Cross Bleed Valve is operative, Wing cross bleed selector switch is selected to the opposite side (FROM LEFT or FROM RIGHT), and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). | ¦ |
|  | 3) Outboard (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 4 | 2 | (O) One element per sensor pair may be inoperative. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-4 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 12-05 | Wing Cross Bleed Valve (Anti-Ice) (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M) May be inoperative CLOSED provided: Both Wing Anti-Ice Modulating SOV’s are operative, Wing Cross Bleed Valve is secured closed, Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. | ¦ |
|  | (600-2C10, 600-2D15, 600-2D24 without ModSum 670T11216) | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: Wing Cross Bleed Valve is secured open, Air Conditioning Pack on the non-selected side is operative and is operated continuously throughout flight, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). | ¦ |
|  | (600-2C10, 600-2D15, 600-2D24 with ModSum 670T11216), (600-2E25) | C | 1 | 0 | (M) May be inoperative OPEN provided: Wing Cross Bleed Valve is secured open, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). | ¦ ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 12-06 | Anti-Ice / Bleed Leak Detection Controller (AILC) Channels (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 |  | ¦ |
| 12-07 | BLEED AIR 14th Stage ISOL "OPEN" Switch Light (light function only) (600-2B19) | C | 1 | 0 |  |  |
| 12-08 | Outboard Low Heat Switches (600-2B19 with ModSum TC601R17364 or TC601R17494) | C | 4 | 0 | (O) May be inoperative provided: Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. | ¦ ¦¦ ¦ |
|  |  | C | 4 | 2 | (M) One switch per wing maybe inoperative provided: Switch failed in closed state is deactivated, and Remaining switch is verified operative. | ¦ ¦¦ ¦ |
| 22-01 | Engine Cowl Anti-Ice SOVs | C | 2 | 1 | (M) One may be inoperative provided: Valve is secured CLOSED, Both Ice Detection Systems are operative, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Limitations. |  |
| 22-02 | Engine Cowl Anti-Ice Pressure Relief Valves (Blow-Off Valves) (600-2B19) | B | 2 | 1 | One may be inoperative OPEN provided: Both Ice Detection Systems are operative, Associated Thrust Reverser is operative, Associated Bleed Air 14th Stage SOV is operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 22-02 | Engine Cowl Anti-Ice Pressure Relief Valves (Blow-Off Valves) (600-2B19) (cont’d) | C | 2 | 1 | May be inoperative OPEN provided: Associated Engine Cowl Anti-Ice SOV is selected OFF, Both Ice Detection Systems are operative, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Limitations. |  |
| 22-03 | Cowl Anti-Ice Double Wall Duct Pressure Transducers (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | May be inoperative provided: Associated Engine Cowl Anti-Ice SOV is selected OFF and considered inoperative, Both Ice Detection Systems are operative, and Operations are not conducted in known or forecast icing conditions. | ¦ |
| 31-01 | Probe Heaters |  |  |  |  |  |
|  | 1) Pitot/Static Probe Heaters | B | 2 | 1 | (M) Except where enroute operations require its use, one may be inoperative provided: Standby Pitot Head Heater is operative, Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
|  | 2) Static Port Heaters | B | 2 | 1 | (M) Except where enroute operations require its use, one may be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 31-01 | Probe Heaters (cont’d) |  |  |  |  |  |
|  | 3) Angle-of-Attack Vane Heaters | B | 2 | 1 | (M) One may be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
|  | 4) TAT Probe Heater |  |  |  |  |  |
|  | a) 600-2B19 | C | 1 | 0 | (M) May be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
|  | b) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | B | 1 | 0 | (M) May be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, Operations are conducted in day VMC conditions only, and Both engines T2 sensors and T2 heaters are operative. (cont’d) | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-8 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 31-01 | Probe Heaters (cont’d) |  |  |  |  |  |
|  | 5) Base Heaters (600-2B19) | B | 2 | 0 | (M) May be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
|  | 6) Standby Pitot Head Heater | B | 1 | 0 | (M) May be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
|  | 7) Engine T2 Probe Heaters (600-2C10, 600-2D15, 600-2D24, 600-2E25) | B | 2 | 1 | (M) May be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. | ¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-9 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 31-02 | Air Data Sensor Heater Controllers | B | 3 | 2 | (M) One may be inoperative provided: Operations are not conducted in visible moisture (including standing water and slush) in any form, Operations are not conducted in known or forecast icing conditions, Both Ice Detection Systems are operative, and Operations are conducted in day VMC conditions only. |  |
| 41-01 | Windshield and Side Window Anti-Ice Controllers | C | 4 | 3 | (M) One may be inoperative provided: Operations are not conducted in known or forecast icing conditions, and Pilot's (Left) side window heating is operative. |  |
|  |  | C | 4 | 2 | (M) Two may be inoperative provided: Operations are not conducted in known or forecast icing conditions, Pilot's (Left) Side window heating is operative, and Both Ice Detection Systems are operative. |  |
| 42-01 | Windshield Wipers | C | 2 | 0 | One or both may be inoperative provided operations are not conducted in precipitation within 5 miles of airport of take-off or intended landing. |  |
|  | 1) 600-2B19 |  |  |  |  |  |
|  | a) SLOW Function | C | 1 | 0 | May be inoperative provided FAST function is operative. |  |
|  | b) FAST Function | C | 1 | 0 | May be inoperative provided SLOW function is operative. |  |
|  | c) PARK Function | C | 1 | 0 | May be inoperative provided wipers can be parked out of pilot’s view. (cont’d) |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-10 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 42-01 | Windshield Wipers (cont’d) |  |  |  |  |  |
|  | 600-2C10, 600-2D15, 600-2D24 600-2E25 |  |  |  |  | ¦ |
|  | a) INT Function | C | 1 | 0 | May be inoperative provided FAST or SLOW function is operative. |  |
|  | b) SLOW Function | C | 1 | 0 | May be inoperative provided FAST function is operative. |  |
|  | c) FAST Function | C | 1 | 0 | May be inoperative provided SLOW function is operative. |  |
|  | d) PARK Function | C | 1 | 0 | May be inoperative provided wipers can be parked out of pilot’s view. |  |
| 71-01 | Aft Waste Service Panel Heater (600-2B19) | C | 1 | 0 |  |  |
| 71-02 | Drain Mast Heater | C | - | 0 | (M) May be inoperative provided: Associated sink is not used, and Sink and/or coffee water supply is turned off. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-11 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 71-03 | Potable Water Freeze Protection Systems (600-2B19) |  |  |  |  |  |
|  | 1) Galley Water System Freeze Protection (excluding Water Tank Heater) | C | 1 | 0 | (M) May be inoperative provided Galley Water Tank is drained. |  |
|  | 2) Lavatory Water System Freeze Protection (excluding Water Tank Heater) | C | 1 | 0 | (M) May be inoperative provided Lavatory Water Tank is drained. |  |
|  | 3) Galley Water Tank Heater | C | 1 | 0 | (M) May be inoperative provided: Heater is deactivated, and Galley water system is drained if ground operations below 0 degrees Celsius (32 degrees Fahrenheit) ambient will exceed 3 hours. |  |
|  | 4) Lavatory Water Tank Heater | C | 1 | 0 | (M) May be inoperative provided: Heater is deactivated, and Lavatory water system is drained. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 30-12 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 30 – ICE AND RAIN |  |  | 4. Remarks or Exceptions |
| PROTECTION |  |  | Remarques ou exceptions |
| 81-01 | Ice Detection Systems | C | 2 | 1 | (M) One may be inoperative provided wing and cowl anti-ice systems are turned ON when icing conditions as defined in the AFM exist or are anticipated. |  |
|  |  | C | 2 | 0 | (M) Both may be inoperative provided: Operations are not conducted in known or forecast icing conditions, and Wing and cowl anti-ice systems are turned ON when icing conditions as defined in the AFM exist or are anticipated, or when any ice build-up on the aircraft is observed. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 2 | 0 | (M) Both may be inoperative provided: Operations are conducted during the day, Wing and cowl anti-ice systems are turned ON when icing conditions as defined in the AFM exist or are anticipated, or when any ice build-up on the aircraft is observed, and Repairs are made within one flight day. | ¦ |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 31-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 31 – INDICATING/ |  |  | 4. Remarks or Exceptions |
| RECORDING SYSTEMS |  |  | Remarques ou exceptions |
| 14-01 | Master Warning Switch Lights (Glareshield) (light function only) | C | 2 | 1 |  |  |
| 14-02 | Master Caution Switch Lights (Glareshield) (light function only) | C | 2 | 1 |  |  |
| 21-01 | Clocks | C | 2 | 1 | As required by Regulations. |  |
|  |  | A | 2 | 0 | (O) Both may be inoperative provided: Both pilot and co-pilot have ready access to a reliable timepiece which display seconds (a wristwatch is acceptable), FDR is considered inoperative, and Repairs are made within three flight days. |  |
| 31-01 | Flight Data Recorder (FDR) | A | 1 | 0 | May be inoperative provided: Cockpit Voice Recorder (CVR) is operative, and Repairs are made within three flight days. |  |
|  | 1) DFDR Recording Parameters required by Regulations | A | - | - | Up to three digital recording parameters may be inoperative provided: Cockpit Voice Recorder (CVR) is operative, and Repairs are made within twenty calendar days. | ¦ |
|  | 2) DFDR Recording Parameters not required by Regulations | A | - | - | May be inoperative provided repairs are made before the completion of the next heavy maintenance visit. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 31-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 31 – INDICATING/ |  |  | 4. Remarks or Exceptions |
| RECORDING SYSTEMS |  |  | Remarques ou exceptions |
| 31-02 | Quick Access Recorder (QAR) *** | D | 1 | 0 |  |  |
| 41-01 | Data Concentrator Units (DCUs) |  |  |  |  |  |
|  | 1) 600-2B19 | C | - | 2 | (M) May be inoperative provided: The inoperative DCU is deactivated, Associated AUDIO WARNING DISABLE switch is selected, and Two separate audio warning channels are verified operative before each flight. NOTE 1: In the event of a DCU1 failure both Master Warning and Master Caution lights will not test during the Lamp 1 test. NOTE 2: In the event of a DCU2 failure, Master Warning and Master Caution lights will not test during the Lamp 2 test. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | - | 2 | (M) May be inoperative provided: The inoperative DCU is deactivated, and Associated AUDIO WARNING DISABLE switch is selected. NOTE 1: In the event of a DCU1 failure both Master Warning and Master Caution lights will not test during the Lamp 1 test. NOTE 2: In the event of a DCU2 failure, Master Warning and Master Caution lights will not test during the Lamp 2 test. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 31-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 31 – INDICATING/ |  |  | 4. Remarks or Exceptions |
| RECORDING SYSTEMS |  |  | Remarques ou exceptions |
| 41-02 | EICAS Control Panel (ECP) Discrete Buttons | B | 1 | 0 | Each may be inoperative provided PRIM, STAT, CAS and STEP buttons are verified operative. |  |
|  | a) ECS |  |  |  |  |  |
|  | b) HYD |  |  |  |  |  |
|  | c) ELEC |  |  |  |  |  |
|  | d) FUEL |  |  |  |  |  |
|  | e) F/CTL |  |  |  |  |  |
|  | f) A/ICE |  |  |  |  |  |
|  | g) DOORS |  |  |  |  |  |
|  | h) SEL |  |  |  |  |  |
|  | i) MENU |  |  |  |  |  |
|  | j) UP |  |  |  |  |  |
|  | k) DN |  |  |  |  |  |
| 41-03 | Lamp Driver Unit Channels | C | 2 | 1 | (M) One channel may be inoperative provided: Affected channel is deactivated, and Remaining channel is tested operative. |  |
| 41-04 | Data Concentration Units (DCU) Fans | C | - | 0 |  |  |
| 41-05 | AUDIO WARNING DCU 1/2/3 Switch Guards | C | - | 1 | May be inoperative provided DCU associated with operative switch guard is operative. |  |
| 61-01 | EICAS Display Units (ED #1 or ED#2) | B | 2 | 1 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 31-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 31 – INDICATING/ |  |  | 4. Remarks or Exceptions |
| RECORDING SYSTEMS |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 30-01 | Landing Gear Retraction System |  |  |  |  |  |
|  | 1) 600-2B19 | B | 1 | 0 | (M) May be inoperative provided: Operations are conducted in accordance with AFM Supplement (Flight with Landing Gear Down), Operations are not conducted in known or forecast icing conditions, Ground lock pins are installed to ensure that all three landing gears are locked down throughout flight, Inflight performance information given in Flight Planning and Cruise Control Manual is used, Extended overwater operations are prohibited, Both headsets are worn, Flight Compartment and Cabin Interphone systems are operative, Both Flap Electronic Control Unit Channels are operative, Both Flap Power Drive Unit Motors are operative, and Cat II and Cat III A operations are prohibited. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-2 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 30-01 | Landing Gear Retraction System (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10 600-2D15, 600-2D24, 600-2E25 | B | 1 | 0 | (M) May be inoperative provided: Operations are conducted in accordance with AFM Supplement (Flight with Landing Gear Down), Operations are not conducted in known or forecast icing conditions, Ground lock pins are installed to ensure that all three landing gears are locked down throughout flight, Inflight performance information given in the Flight Planning and Cruise Control Manual (FPCCM) or the Computerized In–Flight Performance (CIFP) is used, Extended over water operations are prohibited, Both headsets are worn, Flight Compartment and Cabin Interphone systems are operative, Both Flap Channels of the Slat Flap Electronic Control Unit are operative, Both Flap Power Drive Unit Motors are operative, Both Slat Channels of the Slat Flap Electronic Control Unit are operative, Both Slat Power Drive Unit Motors are operative, and Cat II and Cat III A operations are prohibited. | ¦ ¦¦¦¦ |
| 31-01 | Landing Gear Selector Handle Anti-Retraction Mechanism | C | 1 | 0 | (M) May be inoperative in LOCKED position (down) provided downlock release mechanism is verified operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 40-01 | Tire Pressure Indicators *** (600-2C10, 600-2D15, 600-2D24, 600-2E25) | D | 6 | 0 | (M) | ¦ |
| 42-01 | Nose Wheel Spin Down Straps (600-2C10, 600-2D15, 600-2D24) | C | 2 | 0 | (M)(O) May be inoperative provided: Straps are removed, and Nose wheel tires are visually checked for damage. |  |
| 43-01 | Brake Accumulator Pressure Gauges | C | 2 | 0 | (M) Both may be inoperative provided accumulator pre-charge pressure is checked using a suitable pressure gauge. |  |
| 44-01 | Anti-skid (System) Channels |  |  |  |  |  |
|  | 1) 600-2B19, 600-2C10 | B | 2 | 1 | (M)(O) Either the inboard or outboard channel may be inoperative provided: Nosewheel Steering is operative, Both pairs of Ground Spoilers are operative, Both Thrust Reversers are operative, Both inboard and outboard wheel brakes are verified operative, Both EICAS Brake Temperature Monitoring Readouts associated with the operative anti-skid channel are operative, Reduced thrust take-off operations are prohibited, Take-off or landing is not conducted from a contaminated runway, and Operations are conducted in accordance with AFM Supplement (Operations with Anti-Skid Inoperative). (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 44-01 | Anti-skid (System) Channels (cont’d) |  |  |  |  |  |
|  | 2) 600-2D15, 600-2D24 | B | 2 | 1 | (M)(O) Either the inboard or outboard channel may be inoperative provided: Nosewheel Steering is operative, Both pairs of Ground Spoilers are operative, Both Thrust Reversers are operative, Both inboard and outboard wheel brakes are verified operative, Both EICAS Brake Temperature Monitoring Readouts associated with the operative anti-skid channel are operative, Reduced thrust take-off operations are prohibited, Take-off is not conducted from a wet runway, Take-off or landing is not conducted from a contaminated runway, and Operations are conducted in accordance with AFM Supplement (Operations with Anti-Skid Inoperative). |  |
|  | 3) 600-2E25 | B | 2 | 1 | (M)(O) Either the inboard or outboard channel may be inoperative provided: Nosewheel Steering is operative, Both pairs of Ground Spoilers are operative, Both Thrust Reversers are operative, Both inboard and outboard wheel brakes are verified operative, Both EICAS Brake Temperature Monitoring Readouts associated with the operative anti-skid channel are operative, Reduced thrust take-off operations are prohibited, Take-off is not conducted from a wet runway, Take-off or landing is not conducted from a contaminated runway, The anti-skid system must be armed for take-off and landing, and Operations are conducted in accordance with AFM Supplement (Operations with Anti-Skid Inoperative). | ¦¦ ¦ ¦ ¦ ¦¦ ¦¦¦ ¦¦ ¦ ¦¦ ¦¦ ¦¦¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 45-01 | Parking Brake Handle Locking Positions (clockwise and counter-clockwise) | B | 2 | 1 | (O) May be inoperative provided: Parking brake system is verified operative, Remaining locking position is verified operative before each flight, and Inoperative locking position is legibly placarded. |  |
| 46-01 | EICAS Brake Temperature Monitoring Readouts | C | 4 | 0 | (M) May be inoperative provided: AFM quick turn-around landing weight charts are used, and Minimum brake cooling times (AFM Performance) are observed. |  |
| 46-02 | A/SKID Sub-system (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (M)(O) May be inoperative as indicated by "A/SKID FAULT" status message on EICAS. | ¦ |
| 47-01 | EICAS Brake Pressure Readouts | C | 2 | 0 | (M) Both may be inoperative provided: Brake accumulator(s) nitrogen pressure is checked prior to the first flight of the day, Capability of brake accumulators to retain adequate hydraulic fluid for brakes is verified prior to the first flight of the day, and EICAS Hydraulic Pressure Readouts are operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 32-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 32 – LANDING GEAR |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 50-01 | Nosewheel Steering |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M)(O) May be inoperative provided: Solenoid selector valve is not failed OPEN, Landing gear selector valve is verified operative, Nosewheel steering system is selected OFF, Take-off or landing is not conducted from a contaminated runway, Flight/Ground Spoiler Systems are operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems inoperative). NOTE: Asymmetric brakes rather than asymmetric thrust should be used to maintain directional control as required at low speed end of the roll. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (M)(O) May be inoperative provided: Solenoid selector valve is not failed OPEN, Landing gear selector valve is verified operative, Nosewheel steering system is selected OFF, Take-off or landing on contaminated runway is prohibited, Both pairs of Ground Spoilers are operative, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems inoperative). NOTE: Asymmetric brakes rather than asymmetric thrust should be used to maintain directional control as required at low speed end of the roll. | ¦ ¦¦ |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Cockpit/ Flight Deck/ Flight Compartment and Instrument Lighting Systems (excluding EFIS) | C | - | - | Individual lights may be inoperative provided remaining lights are: Sufficient to clearly illuminate all required instruments, controls, and other devices for which it is provided, Positioned so that direct rays are shielded from flight crew members eyes, and Lighting configuration and intensity is acceptable to the flight crew. |  |
|  |  | D | - | 0 | May be inoperative provided aircraft is not operated at night. |  |
| 13-01 | Cockpit Dome Light |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 3 | 0 |  | ¦ |
| 21-01 | Cabin Interior Lights |  |  |  |  |  |
|  | 600-2B19 |  |  |  |  |  |
|  | a) A/c without ModSum TC601R101452, or TC601R101462, or TC601R101520 | C | - | - | May be inoperative provided: Sufficient lighting is operative for cabin crew to perform required duties, and Lighting configuration at dispatch is acceptable to the flight crew. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-01 | Cabin Interior Lights (cont’d) |  |  |  |  |  |
|  | 600-2B19 (cont’d) |  |  |  |  |  |
|  | b) A/c with or without ModSum TC601R101576 and either ModSum TC601R101452, or TC601R101462, or TC601R101520 | C | - | - | (O) Up to 25% of galley light individual lamps, up to 25% of sidewall downwash lights, up to 25% of ceiling lights may be inoperative provided: No more than two adjacent and no opposite ceiling lights may be inoperative, No more than two adjacent and no opposite sidewall downwash lights may be inoperative, Cabin interior light brightness control is operative or failed in a bright state, Sufficient lighting is operative for cabin crew to perform required duties, Lighting configuration at dispatch is acceptable to the flight crew, and Procedures for charging the Photoluminescent Floor Proximity Emergency Escape Path Marking System before the first flight of the day are observed. |  |
|  | c) A/c with ModSum TC601R101576 and either ModSum TC601R101452, or TC601R101462, or TC601R101520 | C | - | - | (O) Up to 25% of galley light individual lamps, up to 25% of sidewall downwash lights may be inoperative provided: All ceiling lights are operative, No more than two adjacent and no opposite sidewall downwash lights may be inoperative, Cabin interior light brightness control is operative or failed in a bright state, Sufficient lighting is operative for cabin crew to perform required duties, Lighting configuration at dispatch is acceptable to the flight crew, and Procedures for charging the Photoluminescent Floor Proximity Emergency Escape Path Marking System before the first flight of the day are observed. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-01 | Cabin Interior Lights (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | a) A/c with Fluorescent Lights | C | - | - | All sidewall downwash lights and up to 50% of ceiling lights may be inoperative provided: No more than two adjacent and no opposite ceiling lights may be inoperative, Cabin interior light brightness control is operative or failed in a bright state, Sufficient lighting is operative for cabin crew to perform required duties, and Lighting configuration at dispatch is acceptable to the flight crew. |  |
|  | b) A/c with LED Lights | C | - | - | (O) Up to 50% of total length of ceiling upwash lights and of sidewall downwash lights may be inoperative provided: Inoperative lighting configuration is verified acceptable, Brightest state of cabin interior light brightness control is available, Sufficient lighting is operative for cabin crew to perform required duties, and Lighting configuration at dispatch is acceptable to the flight crew. |  |
| 21-02 | Stair Lights | D | 3 | 0 |  |  |
| 23-01 | Boarding Lights (600-2B19) | D | - | 0 |  |  |
| 23-02 | Entrance Lights (600-2C10, 600-2D15, 600-2D24, 600-2E25) | D | 3 | 0 | May be inoperative provided sufficient lighting for cabin crew is available to perform required duties. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 24-01 | Passenger Notice System (No Smoking/ Fasten Seat Belts) | A | 1 | 0 | (O) May be inoperative provided: Aircraft crew are the only occupants of the aircraft, Alternate procedures are established and used, and Repairs are made within one flight day. NOTE: For the purpose of this item "aircraft crew" is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. |  |
|  |  | C | 1 | 0 | (O) May be inoperative provided: PA system is operative, and Procedures are established and used to alert flight attendants and notify passengers when seat belts are to be fastened and smoking is prohibited. |  |
|  | 1) Automatic Function | C | 1 | 0 | (O) May be inoperative provided: Manual control function is verified operative, and Alternate procedures are established and used. |  |
|  | No Smoking / Fasten Seat Belt Signs | C | - | 0 | (O) May be inoperative provided: PA system is operative, and Procedures are established and used to alert flight attendants and notify passengers when seat belts are to be fastened and smoking is prohibited. |  |
|  |  | C | - | - | (O) One or more may be inoperative provided passenger or flight attendant seats from which a sign is illegible or missing shall not be occupied and must be blocked and placarded "DO NOT OCCUPY". |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-5 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Service Lights | D | - | 0 |  |  |
| 32-01 | Maintenance Lights | D | - | 0 |  |  |
| 41-01 | Landing Lights |  |  |  |  |  |
|  | 1) 600-2B19 | C | 4 | 3 |  |  |
|  |  | C | 4 | 2 | Two may be inoperative provided: Both Taxi/Recognition Lights are operative, and Taxi/Recognition Lights are switched OFF whenever airplane is stationary in excess of 10 minutes. |  |
|  |  | C | 4 | 0 | All may be inoperative provided aircraft is not operated at night. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | Nose Light | C | 1 | 0 | May be inoperative provided: Both Wing Landing Lights are operative, and Both Taxi/Recognition Lights are operative. |  |
|  |  | C | 1 | 0 | May be inoperative provided aircraft is not operated at night. |  |
|  | Wing Lights | C | 2 | 1 | One may be inoperative provided the associated Taxi/Recognition Light is operative. |  |
|  |  | C | 2 | 0 | Both may be inoperative provided aircraft is not operated at night. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-6 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-02 | Taxi/Recognition Lights | C | 2 | 0 | Both may be inoperative provided aircraft is not operated at night. |  |
|  | 1) 600-2B19 | C | 2 | 0 | Both may be inoperative provided two Landing Lights are operative. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 2 | 0 | Both may be inoperative provided all Landing Lights are operative. | ¦ |
| 41-03 | Pulsating Landing Lights System *** (600-2B19) | D | 1 | 0 | (M) May be inoperative provided: System is deactivated, and Landing Light System is verified operative. |  |
| 42-01 | Navigation Lights |  |  |  |  |  |
|  | 1) Wing Tip Position Light Bulbs | C | 4 | 2 | (O) One light bulb may be inoperative at each wing tip. |  |
|  |  | C | 4 | 0 | All may be inoperative provided aircraft is not operated at night. |  |
|  | 2) Aft Position Light Bulbs | C | 2 | 1 | (O) One light bulb may be inoperative provided remaining light bulb is operative. |  |
|  |  | C | 2 | 0 | Both may be inoperative provided aircraft is not operated at night. |  |
| 43-01 | Wing Inspection Lights | C | 2 | 0 | Both may be inoperative provided: Ground de-icing procedures do not require their use, and A portable lamp/light of adequate capacity for wing and/or control surface inspection is available for night operations in icing conditions. |  |
|  |  | C | 2 | 0 | Both may be inoperative provided aircraft is not operated at night. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-7 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 44-01 | High Intensity Anti-Collision Strobe Lights | C | 3 | 0 | May be inoperative provided aircraft is not operated at night. |  |
| 44-02 | Low Intensity Red Beacon Lights | C | 2 | 0 |  |  |
| 45-01 | Sterile Light System *** | D | 1 | 0 | (O) May be inoperative provided alternate procedures are established and used. |  |
| 46-01 | Tail Flood Lights (Logo Lights) *** | D | 2 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-8 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights | A | - | 0 | (O) May be inoperative provided: Aircraft crew are the only occupants of the aircraft, No crew occupies area of affected lights, Alternate procedures are established and used, and Repairs are made within one flight day. NOTE: For the purpose of this item "aircraft crew" is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. |  |
|  | 1) 600-2B19 |  |  |  |  |  |
|  | Ceiling Level Emergency Floodlights | C | 4 | 2 | Two ceiling floodlights may be inoperative provided they are not adjacent to each other. |  |
|  | Floor Level Emergency Floodlights (A/c without ModSum, TC601R101462 or TC601R101470 or TC601R101520) | C | 2 | 2 | Three out of five bulbs within each floodlight may be inoperative. |  |
|  | Floor Level Emergency Floodlights (A/c with ModSum, TC601R101462 or TC601R101470 or TC601R101520) | C | 1 | 1 | Three out of five bulbs within the floodlight may be inoperative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-9 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 1) 600-2B19 (cont’d) |  |  |  |  |  |
|  | Ceiling Level Lighted Exit Signs (Curved Signs) | C | 3 | 3 | Each exit-sign may have 50% of its internal lights inoperative, except that both tip lights in exit sign must be operative. |  |
|  | Lighted Exit Signs | C | 4 | 4 | Each exit sign may have 50% of its internal lights inoperative. |  |
|  | Floor Level Lighted Exit Signs (A/c with ModSum, TC601R101462 or TC601R101470 or TC601R101520) | C | 4 | 4 | Three out of five bulbs within each sign may be inoperative. |  |
|  | Electrolumines- cent Floor Proximity Emergency Escape Path Marking System (A/c without ModSum TC601R101452, or TC601R101462, or TC601R101520) | C | 1 | 1 | Up to 50% of the individual floor-mounted lighting strips may be inoperative provided they are not adjacent to each other. Strips with orange overlays at the Service Door must be operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-10 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 600-2B19 (cont’d) |  |  |  |  |  |
|  | Photolumines-cent Floor Proximity Emergency Escape Path Marking System Strip/Tape *** (A/c with ModSum TC601R101452, or TC601R101462, or TC601R101520) | C | 1 | 1 | May be damaged or segment(s) missing provided: Length of the affected section(s) does not exceed 8 in. (20 cm), Affected section(s) is not attached to the overwing exit marker cross sections, Overwing exit marker cross sections are not affected, Aft cabin cross-aisle section is not affected, Interval between affected sections on the same side is not less than 128 in. (326 cm), Interval between affected sections on the opposite sides is not less than 60 in. (153 cm), and Maximum total length of the affected sections on both sides does not exceed 48 in. (120 cm). NOTE: For the purpose of this item, the term “damaged” implies a degradation of the path marking system strip/tape that prevents the system to perform its intended functions (permanent stain masking the path marking system strip/tape). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-11 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 600-2C10 |  |  |  |  |  |
|  | Ceiling Level Emergency Floodlights | C | - | - | Two lights may be inoperative provided they are not adjacent to each other. |  |
|  | Floor Level Emergency Floodlights | C | 2 | 0 |  |  |
|  | Ceiling Level Lighted Exit Signs (Curved Signs) | C | 3 | 3 | Each exit locator may have 50% of its internal lights inoperative, except that tip lights in exit sign must be operative. |  |
|  | Lighted Exit Signs | C | 4 | 4 | Each exit sign may have 50% of its internal lights inoperative. |  |
|  | Floor Level Lighted Exit Signs | C | 4 | 4 | Each floor proximity exit sign may have 50% of its internal lights inoperative. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-12 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 600-2C10 (cont’d) |  |  |  |  |  |
|  | Photolumines-cent Floor Proximity Emergency Escape Path Marking System Strip/Tape | C | 1 | 1 | May be damaged or segment(s) missing provided: Length of the affected section(s) does not exceed 8 in. (20 cm), Affected section(s) is not attached to the overwing exit marker cross sections, Overwing exit marker cross sections are not affected, Interval between affected sections on the same side is not less than 128 in. (326 cm), Interval between affected sections on the opposite sides is not less than 60 in. (153 cm), and Maximum total length of the affected sections on both sides does not exceed 72 in. (180 cm). NOTE: For the purpose of this item, the term “damaged” implies a degradation of the path marking system strip/tape that prevents the system to perform its intended functions (permanent stain masking the path marking system strip/tape). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-13 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 600-2D15, 600-2D24, |  |  |  |  |  |
|  | Ceiling Level Emergency Floodlights | C | 8 | 5 | Three lights may be inoperative provided they are not adjacent to each other. |  |
|  | Floor Level Emergency Floodlights | C | 2 | 0 |  |  |
|  | Ceiling Level Lighted Exit Signs (Curved Signs) | C | 3 | 3 | Each exit locator may have 50% of its internal lights inoperative, except that tip lights in exit sign must be operative. |  |
|  | Lighted Exit Signs | C | 6 | 6 | Each exit sign may have 50% of its internal lights inoperative. |  |
|  | Floor Level Lighted Exit Signs | C | 6 | 6 | Each floor proximity exit sign may have 50% of its internal lights inoperative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-14 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 600-2D15, 600-2D24 (cont’d) |  |  |  |  |  |
|  | Photolumines-cent Floor Proximity Emergency Escape Path Marking System Strip/Tape | C | 1 | 1 | May be damaged or segment(s) missing provided: Length of the affected section(s) does not exceed 8 in. (20 cm), Affected section(s) is not attached to the overwing exit marker cross sections, Overwing exit marker cross sections are not affected, Interval between affected sections on the same side is not less than 128 in. (326 cm), Interval between affected sections on the opposite sides is not less than 60 in. (153 cm), and Maximum total length of the affected sections on both sides does not exceed 88 in. (220 cm). NOTE: For the purpose of this item, the term “damaged” implies a degradation of the path marking system strip/tape that prevents the system to perform its intended functions (permanent stain masking the path marking system strip/tape). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-15 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 4) 600-2E25 |  |  |  |  | ¦ |
|  | Ceiling Level Emergency Floodlights | C | - | - | Up to five lights may be inoperative provided they are not adjacent to each other. | ¦¦¦ |
|  | Floor Level Emergency Floodlights | C | 2 | 0 |  | ¦¦¦ |
|  | Ceiling Level Lighted Exit Signs (Curved Signs) | C | 3 | 3 | Each exit locator may have 50% of its internal lights inoperative, except that tip lights in exit sign must be operative. | ¦¦¦¦ |
|  | Lighted Exit Signs | C | - | - | Each exit sign may have 50% of its internal LED lights inoperative. | ¦¦ |
|  | Floor Level Lighted Exit Signs | C | 6 | 6 | Each floor proximity exit sign may have 50% of its internal LED lights inoperative. | ¦¦¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-16 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-01 | Cabin Emergency Lights (cont’d) |  |  |  |  |  |
|  | 4) 600-2E25 (cont’d) |  |  |  |  | ¦ |
|  | Photolumines-cent Floor Proximity Emergency Escape Path Marking System Strip/Tape | C | 1 | 1 | May be damaged or segment(s) missing provided: Length of the affected section(s) does not exceed 8 in. (20 cm), Affected section(s) is not attached to the overwing exit marker cross sections, Overwing exit marker cross sections are not affected, Interval between affected sections on the same side is not less than 128 in. (326 cm), Interval between affected sections on the opposite sides is not less than 60 in. (153 cm), and Maximum total length of the affected sections on both sides does not exceed 88 in. (220 cm). NOTE: For the purpose of this item, the term “damaged” implies a degradation of the path marking system strip/tape that prevents the system to perform its intended functions (permanent stain masking the path marking system strip/tape). | ¦ ¦¦ ¦¦ ¦¦ ¦¦ ¦¦¦ ¦¦ ¦¦¦¦¦¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-17 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | Exterior Emergency Lights | C | - | 0 | All may be inoperative provided aircraft is not operated at night. |  |
|  |  | A | - | 0 | (O) May be inoperative provided: Aircraft crew are the only occupants of the aircraft, Alternate procedures are established and used, and Repairs are made within one flight day. NOTE 1: For the purpose of this item "aircraft crew" is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. NOTE 2: Operators MEL must state maximum number of aircraft crew permitted. |  |
|  | 1) 600-2B19 | C | 8 | 6 | One of two rearward overwing lights on each side of aircraft may be inoperative. |  |
|  | 2) 600-2D15, 600-2D24, 600-2E25 | C | 8 | 6 | Forward overwing emergency light on each side of aircraft may be inoperative. | ¦ |
| 51-03 | Emergency Lights "OFF" Light (light function only) (600-2B19) | C | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 33-18 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 33 – LIGHTS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | Integrated Standby Instruments (ISI) (600-2B19***, 600-2C10, 600-2D15, 600-2D24, 600-2E25) |  |  |  |  | ¦ |
|  | 1) NAV Function | C | 1 | 0 |  |  |
|  | 2) Attitude Function | B | 1 | 0 | May be inoperative provided: Operations are conducted in day VMC, and Source selector is selected to NORMAL with each side fed from its on-side AHRS/IRS. |  |
| 14-01 | Altitude Alerting System | A | - | 0 | Except where enroute operations require its use, may be inoperative provided: Autopilot with altitude hold is operative, and Repairs are made within three flight days. |  |
| 21-01 | Attitude Heading Reference System (AHRS) Fans | C | 2 | 0 |  |  |
| 22-01 | Non-stabilized Magnetic Compass (Standby Compass) | B | 1 | 0 | (O) May be inoperative provided: Any combination of two Gyro or INS (IRU) Stabilized Compass Systems operate normally, and Operations are conducted with Dual Independent Navigation Capability and under Positive Radar Control by ATC on the enroute portion of the flight. |  |
|  |  | B | 1 | 0 | (O) May be inoperative for flights that are entirely within areas of magnetic unreliability provided at least two Stabilized Directional Gyro Systems are installed, operative and used in conjunction with approved Free Gyro Navigation Techniques. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 23-01 | Standby Attitude Indicator (600-2B19) | B | 1 | 0 | May be inoperative provided: Operations are conducted in day VMC, and Source selector is selected to NORMAL with each side fed from its on-side AHRS/IRS. |  |
| 25-01 | Source Select Panel Switches |  |  |  |  |  |
|  | 1) ATTD/HDG, DSPL CONT | C | 2 | 0 | Both may be inoperative provided: PFD/MFD are not selected to a common source, Standby Attitude Indicator/ISI Attitude Function is operative, and Standby Magnetic Compass Indicator is operative. |  |
|  | 2) AIR DATA | C | 1 | 0 | Except where enroute operations require its use, may be inoperative. |  |
| 30-01 | Microwave Landing System (MLS) Receiver *** (600-2B19) | D | - | 0 | As required by Regulations. |  |
| 32-01 | Head-up Guidance System *** | D | 1 | 0 | (M) May be inoperative provided approach procedures are not dependent on its use. |  |
|  |  | C | 1 | 0 | (M) May be inoperative provided routine procedures do not require its use. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 41-01 | Weather Radar System | C | 1 | - | As required by Regulations |  |
| 41-02 | Weather Radar Control Panels | C | - | 1 |  |  |
|  |  | C | - | - | As required by Regulations. |  |
| 42-01 | Ground Proximity Warning System | A | - | 0 | (O) May be inoperative provided: Alternate Procedures are established and used, and Repairs are made within three flight days. |  |
|  | Modes 1-4 (Terrain Avoidance) | A | - | 0 | (O) May be inoperative provided: Alternate Procedures are established and used, and Repairs are made within three flight days. |  |
|  | Test Mode | A | 1 | 0 | May be inoperative provided: GPWS is considered inoperative, and Repairs are made within three flight days. |  |
|  | Glideslope Deviation (Mode 5) | B | 1 | 0 |  |  |
|  | Advisory Callouts (Mode 6) | C | - | 0 | (O) May be inoperative provided alternate procedures are established and used. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 42-01 | Ground Proximity Warning System (cont’d) |  |  |  |  |  |
|  | Windshear Mode (Mode 7) |  |  |  |  |  |
|  | 600-2B19 (a/c without ModSum TC601R15984 and without ModSum TC601R17138) | C | 1 | 0 | (M)(O) May be inoperative provided: Alternate procedures are established and used, Flap position transmitters are verified operative, and Takeoffs and landings are not conducted in known or forecast windshear conditions. |  |
|  | 600-2B19 (a/c with ModSum TC601R15984 or TC601R17138), 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (O) May be inoperative provided: Alternate procedures are established and used, and Takeoffs and landings are not conducted in known or forecast windshear conditions. | ¦ |
|  | Enhanced GPWS Modes *** | C | - | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-5 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 42-02 | GRND PROX TERRAIN Switch Guard *** | C | 1 | 0 |  |  |
| 42-03 | GRND PROX FLAP Switch Guard *** | A | 1 | 0 | May be inoperative provided: Ground Proximity Warning System Modes 1-4 are considered inoperative, and Repairs are made within three flight days. |  |
| 43-01 | Traffic Alert Collision Avoidance System (TCAS II) | B | - | 0 | (M) May be inoperative provided system is deactivated and secured. | ¦ |
|  | Combined Traffic Alert (TA) and Resolution Advisory (RA) Dual Displays *** | C | 2 | 1 | (O) One may be inoperative on non-flying pilot side provided TA and RA elements and audio functions are operative on flying pilot side. |  |
|  | 2) Resolution Advisory (RA) Display System(s) | C | 2 | 1 | (O) One may be inoperative on non-flying pilot side. |  |
|  |  | C | - | 0 | (O) May be inoperative provided: All Traffic Alert (TA) display elements and voice command audio functions are operative, and TA only mode is selected by the crew. |  |
|  | 3) Traffic Alert (TA) Display System(s) | C | - | 0 | (O) May be inoperative provided all installed RA display and audio functions are operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-6 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 44-01 | Radio Altimeter |  |  |  |  |  |
|  | 1) 600-2B19 | C | - | 1 | (M) May be inoperative provided approach minimums are not dependent on its use. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | - | 1 | (M) May be inoperative provided: Approach minimums are not dependent on its use, and Spoiler / Stabilizer Subsystem of SSCS is considered inoperative. NOTE: SPLR/STAB FAULT status message will be displayed on EICAS. | ¦ |
| 44-02 | Radio Altimeter Test Switches |  |  |  |  |  |
|  | 1) Single Radio Altimeter Installation | C | 2 | 1 | One may be inoperative provided RAD ALT test function on the operative side is performed prior to each flight. |  |
|  | 2) Dual Radio Altimeter Installation *** | C | 2 | 1 | One may be inoperative provided: RAD ALT test function on the operative side is performed prior to each flight, and Associated Radio Altimeter with the operative test switch is operative. |  |
| 45-01 | IRS Fan *** (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 0 |  | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 50-01 | Long Range Navigation Systems |  |  |  |  |  |
|  | INS/IRS (Navigation Function only) | C | - | -0 | (O) May be inoperative provided: Procedures do not require its use, Affected IRS Navigation Function is disabled through FMS, and For any IRS in ATT mode, the associated Flight Director Modes are considered inoperative. | ¦ ¦ ¦¦ ¦¦¦ |
|  | LORAN, GPS, etc. | C | - | - | As required by Regulations. | ¦¦ |
| 51-01 | Marker Beacon System | D | 2 | 0 | May be inoperative provided approach procedures do not require its use. |  |
| 51-02 | VHF Navigation Systems (VOR/ILS) | C | 2 | - | (O) Any in excess of those required by Regulations may be inoperative provided it is not powered by the DC Essential Bus. |  |
| 52-01 | Automatic Direction Finding (ADF) System | C | - | - | As required by Regulations. |  |
| 53-01 | Distance Measuring Equipment Systems (DME) | C | 2 | - | As required by Regulations. |  |
| 54-01 | ATC Transponders and Automatic Altitude Reporting Systems | C | - | - | As required by Regulations. |  |
|  |  | D | - | - | Any in excess of those required by Regulations may be inoperative. NOTE: Transponder and Flight Director/ Autopilot must use same side ADC data for RVSM operations. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 34-8 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 34 – NAVIGATION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 61-01 | Flight Management Systems *** | C | - | - | (O) Except where enroute operations require its use, all may be inoperative provided: Alternate procedures are established and used, Alternate means for initializing IRS is available for IRS equipped aircraft, and Both RTUs are operative. |  |
|  | 1) Navigation Databases | C | - | - | (O) May be out of currency provided: Current Aeronautical Charts are used to verify Navigation Fixes prior to dispatch, Procedures are established and used to verify status and suitability of Navigation Facilities used to define route of flight, and Approach Navigation Radios are manually tuned and identified. |  |
| 61-02 | FMS/MDC Data Loader *** | D | 1 | 0 |  |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 35-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 35 – OXYGEN |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Observer’s Oxygen System | B | 1 | 0 | May be inoperative provided: Observer’s seat is not occupied, and A passenger seat in the passenger cabin is made available to a regulatory inspector for performance of official duties. |  |
| 10-02 | “OXY LO PRESS” Caution Message (600-2C10, 600-2D15, 600-2D24, 600-2E25) | B | 1 | 1 | (M)(O) OXY LO PRESS caution message may be displayed provided: Oxygen pressure is checked to be above minimum required oxygen pressure before each flight, Crew oxygen pressure is monitored during flight, EICAS Oxygen Pressure Readout is verified operative, and Manual SOV on the cylinder is checked to be open. | ¦ |
| 11-02 | Oxygen Pressure Switch (600-2C10, 600-2D15, 600-2D24, 600-2E25) | B | 1 | 0 | (M) May be inoperative provided: Oxygen cylinder pre-charged pressure is checked prior to each flight, Oxygen cylinder control valve is verified OPEN prior to each flight, and Pilot and Copilot Masks are verified operative prior to each flight. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 35-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 35 – OXYGEN |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | Flight Crew Oxygen Pressure Indications |  |  |  |  |  |
|  | 1) EICAS Readout | C | 1 | 0 | (M)(O) May be inoperative provided Ground Service Panel Pressure Gauge or Bottle Pressure Gauge is operative and checked prior to each flight. |  |
|  | 2) Ground Service Panel Pressure Gauge | C | 1 | 0 | May be inoperative provided EICAS Readout is operative and checked prior to each flight. |  |
|  |  | C | 1 | 0 | (M) May be inoperative provided Bottle Pressure Gauge is operative and checked prior to each flight. |  |
|  | 3) Bottle Pressure Gauge | C | 1 | 0 |  |  |
| 12-02 | High Pressure Discharge Indicator | C | 1 | 0 | (O) May be damaged or missing provided: Two pressure indications are verified operative after failure occurrence, and Crew oxygen bottle pressure is checked within limits before each flight. |  |
| 20-01 | Passenger Oxygen System | B | 1 | 0 | (O) May be inoperative provided: All components of cabin pressurization warning and indicating systems are operative, Operations are conducted so that minimum enroute altitude is at or below 13,000 ft MSL, Operations are conducted at or below FL 250, Portable oxygen units are provided for all crew members and for 10 percent of the passengers for half an hour (supplemental oxygen), Operational procedures are established to ensure that passengers are appropriately briefed to accommodate revised equipment, and Both Air Conditioning Packs are verified operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 35-3 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 35 – OXYGEN |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 20-01 | Passenger Oxygen System (cont’d) |  |  |  |  |  |
|  | 1) Automatic Deployment | B | 1 | 0 | (M) May be inoperative provided: Manual deployment is operative, and Operations are conducted at or below FL 300. |  |
|  | 2) Passenger Service Units (PSUs) | D | - | 0 | (M)(O) Individual PSUs may be inoperative with no flight altitude restriction provided: Associated seats are blocked and placarded to prevent occupancy, PSUs for flight attendant locations operate normally, and No more than two consecutive banks of seats and their adjacent banks of seats have an inoperative PSU (forward and aft, left and right). |  |
|  | 3) Automatic Opening Feature of Door Latches | B | - | - | (M)(O) May be inoperative provided: The door is confirmed inoperative unlatched, The door is secured closed, The PSU oxygen system is operative, The flight remains at or below FL 300, The manual deployment system is operative, No more than two consecutive banks of seats and their adjacent banks of seats have an inoperative automatic opening feature, and Occupants are briefed on oxygen mask access. NOTE: The method of door closure must not hinder ready access to the first aid oxygen outlet. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 35-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 35 – OXYGEN |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 20-02 | Passenger Oxygen (Masks Deployed) "ON" Light | C | 1 | 0 |  |  |
| 20-03 | Lavatory Passenger Oxygen System | C | - | 0 | (O) May be inoperative provided: Lavatory is not used for any purpose, and Lavatory door is locked and placarded "INOPERATIVE DO NOT ENTER". |  |
|  |  | C | - | 0 | (O) May be inoperative provided flight is conducted at or below FL 250. NOTE: These provisos are not intended to preclude lavatory inspections by a crew member. |  |
| 31-01 | Portable Oxygen Dispensing Units | D | - | - | (M)(O) Any in excess of those required by Regulations may be inoperative provided: Inoperative unit is removed from passenger cabin and its location is placarded INOPERATIVE, or it is removed from the installed location, secured out of sight and the unit and its installed location are placarded INOPERATIVE, Required distribution is maintained, and Procedures are established to alert crew members of inoperative or missing equipment. |  |
| 31-02 | Protective Breathing Equipment | D | - | - | (O) Any in excess of those required by Regulations may be missing or inoperative provided: Required distribution of operative units is maintained throughout the aircraft, Inoperative PBE unit is removed from passenger cabin and its location is placarded INOPERATIVE, or it is removed from the installed location, secured out of sight and the PBE unit and its installed location are placarded INOPERATIVE, and Procedures are established to alert crew members of inoperative or missing equipment. |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-02 | Pressure Regulating SOV (PRSOV) |  |  |  |  |  |
|  | 1) 600-2C10 | C | 2 | 1 | (M)(O) May be inoperative provided: Associated PRSOV is secured CLOSED, Opposite HPV is operative, Opposite Engine Cowl Anti-Ice SOV is operative, APU is operative, APU Load Control Valve is operative, Operations are conducted at or below FL 310, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 2) 600-2D15, 600-2D24 | C | 2 | 1 | (M)(O) May be inoperative provided: Associated PRSOV is secured CLOSED, Opposite HPV is operative, Opposite Engine Cowl Anti-Ice SOV is operative, APU is operative, APU Load Control Valve is operative, Operations are conducted at or below FL 250, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 3) 600-2E25 | C | 2 | 2 | Must be operative for dispatch | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-2 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-03 | High Pressure Valve (HPV) |  |  |  |  |  |
|  | 1) 600-2C10 | C | 2 | 1 | (M)(O) May be inoperative provided: Associated HPV is secured CLOSED, Opposite Engine Cowl Anti-Ice SOV is operative, APU is operative, APU Load Control Valve is operative, Operations are conducted at or below FL 310, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 2) 600-2D15, 600-2D24 | C | 2 | 1 | (M)(O) May be inoperative provided: Associated HPV is secured CLOSED, Opposite Engine Cowl Anti-Ice SOV is operative, APU is operative, APU Load Control Valve is operative, Operations are conducted at or below FL 250, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 3) 600-2E25 | C | 2 | 2 | Must be operative for dispatch | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-3 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-04 | Pack Inlet Pressure Sensors (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 0 |  | ¦ |
| 12-01 | Bleed Air L/R 14th Stage SOVs (600-2B19) | C | 2 | 1 | (M) One may be inoperative provided: Affected valve is secured CLOSED, Both Ice Detection Systems are operative, Associated Thrust Reverser is deactivated, stowed, and LOCKED in forward thrust position, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM performance data for one Thrust Reverser inoperative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-4 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-02 | Bleed Air ISOL Valve (Cross-Bleed Valve) |  |  |  |  |  |
|  | 1) 600-2C10 | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: ISOL valve is secured OPEN, Bleed source selector switch is selected either to L ENG or R ENG, Bleed valves selector switch is selected to MANUAL, PRSOV and HPV on selected side are operative, Operations are conducted at or below FL 310, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 2) 600-2D15, 600-2D24 | C | 1 | 0 | (M)(O) May be inoperative OPEN provided: ISOL valve is secured OPEN, Bleed source selector switch is selected either to L ENG or R ENG, Bleed valves selector switch is selected to MANUAL, PRSOV and HPV on selected side are operative, Operations are conducted at or below FL 250, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | 3) 600-2E25 | C | 1 | 1 | Must be operative for dispatch | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-5 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-01 | Bleed Air Leak Detection System (600-2B19) |  |  |  |  |  |
|  | 10th Stage Sensing Loops (A & B) | C | 2 | 1 | (O) Either loop A or B may be inoperative provided neither loop is failed OPEN. |  |
|  | 14th Stage Sensing Loop | C | 2 | 1 | (M) One may be inoperative provided affected Bleed Air 14th Stage SOV is considered inoperative. |  |
|  | Anti-Ice Sensing Loop | C | 1 | 0 | (M) May be inoperative provided: Wing ANTI-ICE switch is selected OFF, Both Ice Detection Systems are operative, and Operations are not conducted in known or forecast icing conditions. |  |
| 21-02 | BLEED AIR 14th Stage "L/R DUCT FAIL/ CLOSED" Switch Lights (light function only) (600-2B19) | C | 2 | 0 |  |  |
| 21-04 | BLEED AIR 10th Stage "DUCT FAIL/ CLOSED" Switch Lights (light function only) (600-2B19) | C | 2 | 0 |  |  |
| 21-05 | BLEED AIR 10th Stage Isol "OPEN" Switch Light (light function only) (600-2B19) | C | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-6 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-06 | Air Leak Detection System (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 1 | System redundancy may be degraded as indicated by “DUCT MON FAULT” status message. | ¦ |
|  | 1) Anti-Ice Loops | C | 2 | 0 | Both Loops (A and B) may be inoperative provided: Wing ANTI-ICE switch is selected OFF, and Operations are not conducted in known or forecast icing conditions. |  |
|  | 2) Cowl Loops |  |  |  |  |  |
|  | Left | C | 2 | 0 | Both Loops (A and B) may be inoperative provided: At least one Right Cowl Loop is operative, Right Cowl Anti-Ice SOV is operative, Right PRSOV is operative, Right HPV is operative, Left cowl ANTI-ICE switch is selected OFF, and Operations are not conducted in known or forecast icing conditions. |  |
|  | Right | C | 2 | 0 | Both Loops (A and B) may be inoperative provided: At least one Left Cowl Loop is operative, Left Cowl Anti-Ice SOV is operative, Left PRSOV is operative, Left HPV is operative, Right cowl ANTI-ICE switch is selected OFF, and Operations are not conducted in known or forecast icing conditions. (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D215/-2D24/-2E25 | Date: | November 10/10 | 36-7 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-06 | Air Leak Detection System (600-2C10, 600-2D15, 600-2D24, 600-2E25) (cont’d) |  |  |  |  | ¦ |
|  | 3) Bleed Loops |  |  |  |  |  |
|  | Left (600-2C10) | C | 2 | 0 | (O) Both loops (A and B) may be inoperative provided: At least one Right Bleed Loop (A or B) is operative, Right PRSOV is operative, Right HPV is operative, Right Air Conditioning Pack is operative, Bleed source selector switch is selected to the R ENG, Bleed Air ISOL Valve is operative and selected CLOSED, Bleed valves selector switch is selected to MANUAL, APU is operative, APU Load Control Valve is operative, Cross bleed start procedure is not used for engine start, Operations are conducted at or below FL 310, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-8 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-06 | Air Leak Detection System (600-2C10, 600-2D15, 600-2D24, 600-2E25) (cont’d) |  |  |  |  | ¦ |
|  | 3) Bleed Loops (cont’d) |  |  |  |  |  |
|  | Left (600-2D15, 600-2D24) | C | 2 | 0 | (O) Both loops (A and B) may be inoperative provided: At least one Right Bleed Loop (A or B) is operative, Right PRSOV is operative, Right HPV is operative, Right Air Conditioning Pack is operative, Bleed source selector switch is selected to the R ENG, Bleed Air ISOL Valve is operative and selected CLOSED, Bleed valves selector switch is selected to MANUAL, APU is operative, APU Load Control Valve is operative, Cross bleed start procedure is not used for engine start, Operations are conducted at or below FL 250, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | Left (600-2E215) | C | 2 | 2 | Must be operative for dispatch. | ¦¦ |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-9 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-06 | Air Leak Detection System (600-2C10, 600-2D15, 600-2D24, 600-2E25) (cont’d) |  |  |  |  | ¦ |
|  | 3) Bleed Loops (cont’d) |  |  |  |  |  |
|  | Right (600-2C10) | C | 2 | 0 | (O) Both loops (A and B) may be inoperative provided: At least one Left Bleed Loop (A or B) is operative, Left PRSOV is operative, Left HPV is operative, Left Air Conditioning Pack is operative, Bleed source selector switch is selected to the L ENG, Bleed Air ISOL Valve is operative and selected CLOSED, Bleed valves selector switch is selected to MANUAL, APU is operative, APU Load Control Valve is operative, Cross bleed start procedure is not used for engine start, Operations are conducted at or below FL 310, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 36-10 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 36 – PNEUMATIC |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-06 | Air Leak Detection System (600-2C10, 600-2D15, 600-2D24, 600-2E25) (cont’d) |  |  |  |  | ¦ |
|  | 3) Bleed Loops (cont’d) |  |  |  |  |  |
|  | Right (600-2D15, 600-2D24) | C | 2 | 0 | (O) Both loops (A and B) may be inoperative provided: At least one Left Bleed Loop (A or B) is operative, Left PRSOV is operative, Left HPV is operative, Left Air Conditioning Pack is operative, Bleed source selector switch is selected to the L ENG, Bleed Air ISOL Valve is operative and selected CLOSED, Bleed valves selector switch is selected to MANUAL, APU is operative, APU Load Control Valve is operative, Cross bleed start procedure is not used for engine start, Operations are conducted at or below FL 250, Operations are not conducted in known or forecast icing conditions, and Operations are conducted in accordance with AFM Supplement (Operations with Airplane Systems Inoperative). |  |
|  | Right (600-2E25) | C | 2 | 2 | Must be operative for dispatch. | ¦¦ |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 38-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 38 – WATER/WASTE |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Potable Water Systems | C | 2 | 0 | (M)(O) May be inoperative provided: Appropriate procedures are established to deactivate applicable system components to prevent its use or servicing, and Tank is drained and inspected to ensure no leakage. NOTE 1: (600-2C10, 600-2D15, 600-2D24 only) "Diagnostic" light may be illuminated when one or both potable water system is inoperative. NOTE 2: (O) procedure addresses other means for water provision for crew members as well as the need to advise of system status during crew changes. NOTE 3: Aviation Occupatiuonal Health & Safety (AOH&S) requirements should be addressed. | ¦ ¦ ¦¦¦¦ ¦¦¦ |
|  |  | C | - | 0 | (M)(O) Individual components may be inoperative provided: Associated components are deactivated or isolated, and Associated system components are verified not to have leaks. NOTE: Any portion of system which operates normally may be used. |  |
|  | 1) Sub-system Components/ Functions (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | (O) May be inoperative as indicated by the "Diagnostic" light on the Potable Water Control Panel provided both AFT and FWD Potable Water Systems are verified operative. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 38-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 38 – WATER/WASTE |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 30-01 | Lavatory Waste System | C | - | 0 | (M)(O) May be inoperative provided: Procedures are established to deactivate system components, Waste is drained, and system is inspected for leakage, and Lavatory door is locked closed and placarded INOPERATIVE - DO NOT ENTER. NOTE 1: (O) procedure addresses other means for water provision for crew members as well as the need to advise of system status during crew changes. NOTE 2: Aviation Occupatiuonal Health & Safety (AOH&S) requirements should be addressed. | ¦ ¦¦¦¦ ¦¦¦ |
|  | 1) 600-2C10***, 600-2D15***, 600-2D24***, 600-2E25*** | C | 2 | 1 | (M) May be inoperative provided: Procedures are established to deactivate system components, Waste is drained, and system is inspected for leakage, Lavatory door is locked closed and placarded INOPERATIVE - DO NOT ENTER, and There is at least one serviceable lavatory on the aircraft. | ¦ ¦ |
| 30-02 | Lavatory Service Indicator Lights | C | - | 0 | May be inoperative provided alternate procedures are established and used. NOTE: Waste tanks require a precharge of 8.7 L (2.3 US gallons). |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 45-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 45 – CENTRAL |  |  | 4. Remarks or Exceptions |
| MAINTENANCE SYSTEMS |  |  | Remarques ou exceptions |
| 45-01 | Maintenance Diagnostic Computer (MDC) | B | 1 | 0 | (M) May be inoperative provided alternate procedures are established and used. |  |
| 45-02 | MAINT Switch Guard | C | 1 | 0 | May be inoperative, broken or missing. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 45-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 45 – CENTRAL |  |  | 4. Remarks or Exceptions |
| MAINTENANCE SYSTEMS |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 46-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 46 – INFORMATION SYSTEMS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 20-01 | Electronic Flight Bag Systems (EFBs) (Class 2) *** |  |  |  |  |  |
|  | Data Connectivity | C | 2 | 0 | (O) May be inoperative provided alternative procedures are established and used. |  |
|  |  | D | 2 | 0 | May be inoperative provided procedures do not require its use. |  |
|  | Power Connection | C | 2 | 0 | (O) May be inoperative provided alternative procedures are established and used. |  |
|  |  | D | 2 | 0 | May be inoperative provided procedures do not require its use. |  |
|  | Mounting Device | C | 2 | 0 | (M)(O) May be inoperative provided: Associated EFB and hardware is secured by an alternate means or removed from the aircraft, and Alternative procedures are established and used. |  |
|  |  | D | 2 | 0 | (M) May be inoperative provided: Associated EFB and hardware is secured by an alternate means or removed from the aircraft, and Procedures do not require its use. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 46-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 46 – INFORMATION SYSTEMS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Auxiliary Power Unit (APU) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M) May be inoperative provided: APU is deactivated, Intake door is visually verified CLOSED, and Both Integrated Drive Generators (IDG) are operative. |  |
|  |  | C | 1 | 0 | (M) May be inoperative provided: APU is deactivated, Aircraft speed is limited to 300 knots, and Both Integrated Drive Generators (IDG) are operative. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | (M) May be inoperative provided: APU is deactivated, Intake door is visually verified CLOSED, and Both Integrated Drive Generators (IDG) are operative. | ¦ |
|  |  | C | 1 | 0 | (M) May be inoperative provided: APU is deactivated, Aircraft speed is limited to 220 knots, and Both Integrated Drive Generators (IDG) are operative. |  |
|  | 3) 600-2E25 | C | 1 | 0 | (M)(O) May be inoperative provided: APU is deactivated, Intake door is visually verified CLOSED, Both Integrated Drive Generators (IDG) are operative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦¦ ¦¦ |
|  |  |  |  |  | cont’d |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Auxiliary Power Unit (APU) (cont’d) |  |  |  |  |  |
|  | 3) 600-2E25 (cont’d) | C | 1 | 0 | (M)(O) May be inoperative provided: APU is deactivated, Aircraft speed is limited to 220 knots, Both Integrated Drive Generators (IDG) are operative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦¦ ¦¦ |
| 14-01 | APU Air Intake Door Linear Actuator |  |  |  |  |  |
|  | 600-2B19 | C | 1 | 0 | May be inoperative provided: APU is not used, Aircraft speed is limited to 300 knots, and Both Integrated Drive Generators are operative. |  |
|  |  | C | 1 | 0 | (M) May be inoperative provided: Intake door is deactivated CLOSED, and APU is considered inoperative. |  |
|  |  | C | 1 | 0 | (M)(O) May be inoperative provided: Intake door is deactivated OPEN, APU is operated continuously during flight or aircraft speed is limited to 300 knots if APU is OFF, AFM performance corrections for APU ON are applied, APU Battery is operative, and APU Battery Charger is operative. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 14-01 | APU Air Intake Door Linear Actuator (cont’d) |  |  |  |  |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | May be inoperative provided: APU is not used, Aircraft speed is limited to 220 knots, and Both Integrated Drive Generators (IDG) are operative. | ¦ |
|  | 3) 600-2E25 | C | 1 | 0 | (O) May be inoperative provided: APU is not used, Aircraft speed is limited to 220 knots, Both Integrated Drive Generators (IDG) are operative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦¦ ¦¦ |
|  | 4) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | (M) May be inoperative provided: Intake door is deactivated CLOSED, and APU is considered inoperative. | ¦ |
|  |  | C | 1 | 0 | (M) May be inoperative provided: Intake door is deactivated OPEN, APU is operated continuously during flight or aircraft speed is limited to 220 knots if APU is OFF, and AFM performance corrections for APU ON are applied. |  |
|  | 5) 600-2E25 | C | 1 | 0 | (M) May be inoperative provided: Intake door is deactivated OPEN, APU is operated continuously during flight or aircraft speed is limited to 220 knots if APU is OFF, AFM performance corrections for APU ON are applied, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦¦¦ ¦¦ ¦¦ |
|  |  |  |  |  | cont’d |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-4 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 14-01 | APU Air Intake Door Linear Actuator (cont’d) |  |  |  |  |  |
|  | 5) 600-2E25 (cont’d) | C | 1 | 0 | (M) May be inoperative provided: Intake door is deactivated CLOSED, APU is considered inoperative, and Operation is limited to temperature below ISA+30. | ¦ ¦ ¦ ¦¦ |
| 43-01 | APU START/STOP "START/AVAIL" Switch Light (light function only) | C | 1 | 0 |  |  |
| 51-01 | APU Load Control Valve (LCV) |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | (M) May be inoperative provided it is secured CLOSED. NOTE: The APU is available as a source of electrical power only, if required. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24 | C | 1 | 0 | (M) May be inoperative CLOSED provided Bleed Valves are selected to “Manual” on the Bleed Air Control Panel. NOTE: The APU is available as a source of electrical power only, if required. |  |
|  | 3) 600-2E25 | C | 1 | 0 | (M)(O) May be inoperative CLOSED provided Bleed Valves are selected to “Manual” on the Bleed Air Control Panel, and Operation is limited to temperature below ISA+30. NOTE: The APU is available as a source of electrical power only, if required. | ¦ ¦¦ ¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-5 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 51-02 | APU Surge Control Valve (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative CLOSED provided: APU is not operated above 17,000 ft, and Operations are not dependent on use of APU. | ¦ |
| 51-03 | APU LCV “FAIL/OPEN” Switch Light (light function only) (600-2B19) | C | 1 | 0 |  |  |
| 61-01 | Electronic Control Unit (ECU) | C | 1 | 0 | May be inoperative provided APU is considered inoperative. |  |
| 61-02 | APU Sub-system |  |  |  |  |  |
|  | 1) 600-2C10, 600-2D15, 600-2D24 | B | 1 | 0 | (O) May be inoperative as indicated by ”APU FAULT” status message on ground provided: APU is operative (start and shutdown normally), and Flight operations are not dependent on use of APU. |  |
|  | 2) 600-2E25 | B | 1 | 0 | (O) May be inoperative as indicated by ”APU FAULT” status message on ground provided: APU is operative (start and shutdown normally), Flight operations are not dependent on use of APU, and Operation is limited to temperature below ISA+30. | ¦¦ ¦¦ ¦¦ ¦¦ |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 49-6 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 49 – APU |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d’articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Passenger Door Power Assist System | C | 1 | 0 | (M) May be inoperative provided door is verified manually operative (opens and closes) without any interference. NOTE: Stand clear of door when opening. (Door opens faster). |  |
| 11-05 | Passenger Door Handrail Quick- Release Pins (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | (M) May be missing provided the associated cable is stowed. | ¦ |
| 11-06 | Passenger Door Support Wheel Assembly | C | 1 | 0 | (M)(O) May be inoperative or missing provided: Support Wheel Assembly is deactivated, Alternate procedures to support door with cable kit are established and used, and Placarded stairway loading limitations are maintained. |  |
| Aircraft – Aéronef | Revision No – No de révision : | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-01 | Doors and Overwing Emergency Exits | A | - | - | (M)(O) One overwing emergency exit or one door may be inoperative provided: Only aircraft crew are carried, Affected door or emergency exit is verified CLOSED, LATCHED and LOCKED before each departure, Aircraft crew are advised of the nature (emergency exit availability) and extent of the unserviceability and that evacuation procedures do not include affected exit though opposite exit may be used, A conspicuous sign or placard, indicating that the exit is inoperative, is attached to the exit, Emergency exit signs and lights associated with the inoperative exit are obscured, and Repairs are made within three flight days. NOTE 1: Operator’s MEL must state maximum number of aircraft crew permitted, and their seated locations. NOTE 2: For the purpose of this item "aircraft crew" is considered to be flight crew members, flight attendants, aircraft maintenance personnel and supervisory crew members. NOTE 3: Exit locator signs and emergency aisle path markings, which are shared between two exits, must not be obscured. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-3 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Balance Springs |  |  |  |  |  |
|  | 1) Cargo Compartment Door (600-2B19) | C | 2 | 1 | May be inoperative provided door is verified operative (opens and closes) without any interference. NOTE: Door may close faster. |  |
|  | 2) Aft Cargo Compartment Door (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | May be inoperative provided door is verified operative (opens and closes) without any interference. NOTE: Door may close faster. | ¦ |
| 35-01 | Forward Cargo Compartment Protector Kits (600-2C10, 600-2D15, 600-2D24, 600-2E25) |  |  |  |  | ¦ |
|  | 1) A/c without ModSum LE670T11781 (Door Protector Kit) | D | - | 0 | (M) May be inoperative provided: Affected protector kit is removed, Associated cargo compartment door is visually inspected for damage and checked for correct operation, and Associated cargo compartment or sub-compartment remains empty. |  |
|  |  | D | - | 0 | (M) May be inoperative provided: Affected protector kit is removed, Associated cargo compartment door is visually inspected for damage and checked for correct operation, and Associated Cargo Compartment Door Restraint Nets are verified operative and properly installed after every cargo/baggage loading. |  |
|  |  |  |  |  | (cont’d) |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-4 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 35-01 | Forward Cargo Compartment Protector Kits (cont’d) |  |  |  |  |  |
|  | 2) A/c with ModSum LE670T11781 (Vent Flap Protector Kit) | D | - | 0 | (M) May be inoperative provided: Affected protector kit is removed, Associated vent flap mechanism is visually inspected for damage and checked for correct operation, and Associated cargo compartment or sub-compartment remains empty. |  |
|  |  | D | - | 0 | (M) May be inoperative provided: Affected protector kit is removed, Associated vent flap mechanism is visually inspected for damage and checked for correct operation, and Associated Cargo Compartment Door Restraint Nets are verified operative and properly installed after every cargo/baggage loading. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-5 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 70-01 | Passenger Door Indication System |  |  |  |  |  |
|  | 1) 600-2B19 without ModSum TC 601R13193 (Phase IV Door) | A | 1 | 0 | (O) One passenger door EICAS caution message may be continuously displayed provided before each flight: Door is CLOSED, LATCHED and LOCKED, Internal green witness marks on six door latch pins are aligned, Green witness marks on two upper roll latches are aligned, Door lock flag indicator indicates LOCKED, Inner knob is verified STOWED, External handle is verified STOWED, External pressure vent flap is verified fully CLOSED, No door warning EICAS messages are displayed, and Repairs are made within three flight days. |  |
|  | 2) 600-2B19 with ModSum TC 601R13193 (Phase IV Door) | A | 1 | 0 | (O) One passenger door EICAS caution message may be continuously displayed provided before each flight: Door is CLOSED, LATCHED and LOCKED, Internal green witness marks on four door latch pins are aligned, Green witness marks on two upper roll latches are aligned, Green witness mark on upper lock on upper roll shaft is aligned, Door lock flag indicator indicates LOCKED, External handle is verified STOWED, External pressure vent flap is verified fully CLOSED, No door warning EICAS messages are displayed, and Repairs are made within three flight days. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-6 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 70-01 | Passenger Door Indication System (cont’d) |  |  |  |  |  |
|  | 3) 600-2C10, 600-2D15, 600-2D24, 600-2E25 | A | 1 | 0 | (O) One passenger door EICAS caution message may be continuously displayed provided before each flight: Door is CLOSED, LATCHED and LOCKED, Internal green witness marks on four door latch pins are aligned, Green witness marks on two upper roll latches are aligned, Green witness mark on upper lock on upper roll shaft is aligned, Door lock flag indicator indicates LOCKED, External handle is verified STOWED, External pressure vent flap is verified fully CLOSED, No door warning EICAS messages are displayed, Ground Valve (Avionics Cooling) is considered inoperative, and Repairs are made within three flight days. | ¦ |
| 70-02 | Avionic Compartment Door Indication System | C | 1 | 0 | May be inoperative provided before each flight: Door is CLOSED, LATCHED and LOCKED, and Handle is verified STOWED. |  |
| 70-03 | Overwing Emergency Exit Indication Systems | C | - | 0 | (O) May be inoperative provided before each flight: Affected door is CLOSED, LATCHED and LOCKED, and External push plate is verified FLUSH. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-7 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 70-04 | Cargo Compartment Door Indication System |  |  |  |  |  |
|  | 1) FWD (600-2C10, 600-2D15, 600-2D24, with modsum 670T31862), (600-2E25) | C | 1 | 0 | May be inoperative provided before each flight: Door is verified CLOSED, LATCHED and LOCKED, Handle is verified STOWED, External pressure vent flap is verified CLOSED, and Gap between door and fuselage is verified not present. | ¦¦¦¦¦¦¦¦¦ |
|  | 2) CTR (600-2D15, 600-2D24, 600-2E25 with modsum 670T31862), (600-2E25) | C | 1 | 0 | May be inoperative provided before each flight: Door is verified CLOSED, LATCHED and LOCKED, Handle is verified STOWED, External pressure vent flap is verified CLOSED, and Gap between door and fuselage is verified not present. | ¦¦¦¦¦¦¦¦¦ |
|  | 3) AFT | C | 1 | 0 | May be inoperative provided before each flight: Door is verified CLOSED, LATCHED and LOCKED, and Handle is verified STOWED. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 52-8 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 52 – DOORS |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 70-05 | Service Door Indication System |  |  |  |  |  |
|  | 1) 600-2B19 | C | 1 | 0 | May be inoperative provided before each flight: Door is CLOSED, LATCHED and LOCKED, Internal green witness marks are verified aligned at viewing window, Internal handle is verified at LOCKED position, and External handle is verified STOWED. |  |
|  | 2) 600-2C10 | C | 1 | 0 | May be inoperative provided before each flight: Door is CLOSED, LATCHED and LOCKED, Handle is verified STOWED, External pressure vent flap is verified CLOSED, and Ground Valve (Avionics Cooling) is considered inoperative. |  |
|  | 3) FWD (600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 | May be inoperative provided before each flight: Door is CLOSED, LATCHED and LOCKED, Handle is verified STOWED, External pressure vent flap is verified CLOSED, and Ground Valve (Avionics Cooling) is considered inoperative. | ¦ |
|  | 4) AFT (600-2D15***, 600-2D24***) | C | 1 | 0 | May be inoperative provided before each flight: Door is CLOSED, LATCHED and LOCKED, Handle is verified STOWED, External pressure vent flap is verified CLOSED, and Ground Valve (Avionics Cooling) is considered inoperative. |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 73-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 73 – ENGINE FUEL & CONTROL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 21-01 | Full Authority Digital Engine Control System (FADEC) (600-2C10, 600-2D15, 600-2D24, 600-2E25) |  |  |  |  | ¦ |
|  |  | A | 1 | 1 | System redundancy may be degraded as indicated by “L FADEC FAULT 1” status message provided: “R FADEC FAULT 1” status message is not displayed, and Repairs are made within 10 days. |  |
|  |  | A | 1 | 1 | System redundancy may be degraded as indicated by “R FADEC FAULT 1” status message provided: “L FADEC FAULT 1” status message is not displayed, and Repairs are made within 10 days. |  |
|  |  | A | 1 | 1 | (M) System redundancy may be degraded as indicated by “L FADEC FAULT 1” and “R FADEC FAULT 1” status messages provided: Specific FADEC faults listed in the maintenance procedures are verified not present on both engines simultaneously, and Repairs are made within 10 days. |  |
|  |  | A | 1 | 1 | System redundancy may be degraded as indicated by “L FADEC FAULT 2” status message provided repairs are made within 30 days. |  |
|  |  | A | 1 | 1 | System redundancy may be degraded as indicated by “R FADEC FAULT 2” status message provided repairs are made within 30 days. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 73-2 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 73 – ENGINE FUEL & CONTROL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | EICAS Fuel Flow “FF” Readouts (600-2B19) | B | 2 | 1 | May be inoperative provided all EICAS Fuel Tank Quantity Readouts are operative. |  |
| 31-02 | EICAS Fuel Used Readout (600-2B19) | C | 1 | 0 | May be inoperative provided all EICAS Fuel Tank Quantity Readouts are operative. |  |
| 31-03 | Fuel Low Pressure Indicating Systems (600-2B19) | A | 2 | 1 | (O) May be inoperative provided: Both Fuel Boost Pumps are operative, and Repairs are made within two days. NOTE: Fuel system check valve test (First flight of day – Before Engine Shutdown) is waived for the inoperative fuel low pressure indication. |  |
| 31-04 | Fuel Feed Temperature Indicating System | C | 2 | 1 | One may be inoperative provided icing inhibitor is added to the fuel. |  |
|  |  | C | 2 | 1 | May be inoperative provided EICAS oil temperature readout is checked to be stable within limits prior to each flight. |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 74-1 |  |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 74 – IGNITION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 11-01 | Ignition Systems |  |  |  |  |  |
|  | 1) 600-2B19 |  |  |  |  |  |
|  | A Systems | B | 2 | 1 | One may be inoperative provided both B Systems are operative. |  |
|  | B Systems | B | 2 | 0 | Both may be inoperative provided both A Systems are operative. NOTE: Although the Continuous Ignition System remains operative, the “CONT IGNITION” status message and “CONT IGNITION ON” light on overhead panel are inhibited. |  |
|  | 2) 600-2C10, 600-2D15, 600-2D24, 600-2E25 |  |  |  |  | ¦ |
|  | A Systems | B | 2 | 1 | (O) One may be inoperative provided both B Systems are operative. |  |
|  | B Systems | B | 2 | 0 | (O) Both may be inoperative provided both A Systems are operative. |  |
| 30-01 | IGNITION A/B “ARM/ON” Switch Lights (light function only) (600-2B19) | C | 2 | 0 |  |  |
| 30-02 | IGNITION CONT “ON” Switch Light (light function only) | C | 1 | 0 |  |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 74-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 74 – IGNITION |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 76-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 76 – ENGINE CONTROL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-02 | SYNC SEL Switch (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 1 | 0 |  | ¦ |
| 11-01 | L & R Engine Speed Control Systems (600-2B19) | C | 2 | 0 | (O) Both may be inoperative provided: ENG SPEED CONTROL switches are selected OFF for both engines, APR is selected OFF, and Operations are conducted in accordance with AFM APR inoperative performance data. NOTE: Thrust levers will not always be aligned when fan speeds are matched. |  |
| 11-03 | Throttle Lever (FADEC) RVDTs (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 4 | 2 | One per throttle lever may be inoperative. | ¦ |
| 13-01 | Automatic Performance Reserve System (APR) (600-2B19) | C | 1 | 0 | (O) May be inoperative provided: APR is selected OFF, and Operations are conducted in accordance with AFM APR inoperative performance data. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 76-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 76 – ENGINE CONTROL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 77-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 77 – ENGINE INDICATING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 31-01 | Engine Vibration Monitoring Indications | B | 2 | 1 | One may be inoperative provided: Operations are not conducted in known or forecast icing conditions, and Both Ice Detection Systems are operative. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 77-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 77 – ENGINE INDICATING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 78-1 | ¦ |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 78 - EXHAUST |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 30-01 | Thrust Reverser Systems | C | 2 | 1 | (M) One may be inoperative provided: There is no structural damage to thrust reverser system beyond approved acceptable damage limits, Inoperative thrust reverser is deactivated, stowed and locked in forward thrust position, and Operations are conducted in accordance with AFM performance data. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 78-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 78 - EXHAUST |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 79-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 79 - OIL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 12-01 | Oil Replenishment System *** | D | 1 | 0 | (M) May be inoperative provided alternate method for checking engine oil levels and servicing engine oil is established and used. |  |
| 21-01 | Engine Oil Filter Impending Bypass and Chip Detector Panel (Engine Oil Detection Panel) |  |  |  |  |  |
|  | 600-2B19 | C | 1 | 0 | (M) May be inoperative provided the approved maintenance procedure is accomplished and does not exceed 30 flight hours in between. |  |
|  | 600-2C10, 600-2D15, 600-2D24, 600-2E25 | C | 1 | 0 | (M) May be inoperative provided the approved maintenance procedure is accomplished and does not exceed 100 flight hours in between. | ¦ |
| 30-01 | Low Oil Pressure Switch (600-2C10, 600-2D15, 600-2D24, 600-2E25) | A | 2 | 1 | (O) May be inoperative OPEN provided: Both oil pressure readouts are verified operative, and Repairs are made within one flight day. | ¦ |
|  |  | A | 2 | 1 | (M)(O) May be inoperative CLOSED provided: Both oil pressure readouts are verified operative, Inoperative Low Oil Pressure Switch is deactivated, and Repairs are made within one flight day. NOTE: Aural warning "Engine Oil" will not be functional. |  |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 79-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 79 - OIL |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 30-03 | Engine Oil Level Indications (600-2B19***, 600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 0 | (M) Both may be inoperative provided: Engine oil reservoir is refilled within the permissible time interval, and There is no evidence of excessive oil consumption. | ¦ |

| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| --- | --- | --- | --- |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 80-1 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 80 - STARTING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
| 10-01 | Engine L/R “STOP” Switch Lights (light function only) | C | 2 | 0 | Both may be inoperative provided N2 is monitored. |  |
| 10-02 | Engine “START” Switch Lights (light function only) | C | 2 | 0 |  |  |
| 10-03 | Air Turbine Starter Speed Cutout Switches (600-2B19) | C | 2 | 1 | (O) May be inoperative CLOSED provided: Associated Engine STOP Switch Light is operative, Engine start is manually terminated, and Starter disengagement is confirmed. NOTE: The Air Turbine Starter will be damaged if it is left engaged at or above engine idle speed. |  |
| 11-03 | Starter Air Valves (600-2C10, 600-2D15, 600-2D24, 600-2E25) | C | 2 | 1 | (M)(O) One may be inoperative CLOSED provided alternate starting procedures are established and used. | ¦ |
| Aircraft – Aéronef | Revision No - No de révision: | 20 | Page |
| Canadair CL-600-2B19/-2C10/-2D15/-2D24/-2E25 | Date: | November 10/10 | 80-2 |
| 1. | 2. Number Installed |
| System & Sequence No Item | Nombre d’articles installés |
| No de système/série article |  | 3. Number Required For Dispatch |
|  |  | Nombre d'articles à expédier |
| 80 - STARTING |  |  | 4. Remarks or Exceptions |
|  |  |  | Remarques ou exceptions |
|  |  |  |  |  | THIS PAGE INTENTIONALLY LEFT BLANK |  |