Six Sigma as a

Business (Improvement) Strategy

Table of Contents

Page

What is Six Sigma?	4

Why Do It?	5

Macro & Micro Economics of Quality	6

Macroeconomics of Quality	6

Microeconomics of Quality	6

Getting to Six Sigma	7

Six Sigma Deployment	8

Where Can Six Sigma be Applied?	9

Exercises	11

Exercise 1:  Sigma, Process Capability, DPM	12

Exercise 2:  Macroeconomics of Quality	13

Exercise 3:  Microeconomics of Quality	14

Exercise 4:  How Far Can Inspection Get Us?	15

Exercise 5:  Driving Processes through the Numbers	20

Exercise 6:  Changing Habits	29

Charles Oakley, one of the Six Sigma Champions was brought in to provide an overview of Six Sigma to the team.  He explained, “Six Sigma as a data-driven business strategy has really turned into the hot-button issue of the day.  The term itself has turned into the financial equivalent of a Good Housekeeping seal of approval.  First advanced by Motorola around 1986 and advantageously adapted by many organizations, the strategy involves rigorous training in the use of specialized measurement and statistical tools to help improve customer satisfaction by reducing defects in products, processes, and services, cutting costs which are passed on to the customer, and reducing the cycle time and its variation, which translates to on-time delivery.  The list of enterprises adapting the Six Sigma strategy is almost endless and continues to grow, embracing many Fortune 500 companies and their suppliers.  However, those organizations that have deployed it successfully, where it has become part of the corporate culture are relatively few.  GE and Allied Signal fall into this category, which has resulted in a significant increase in their shareholder value.

In order to understand Six Sigma as a business strategy, we need to address several key questions:

- What is it?

- Why do it?

- How can the company get to Six Sigma?

- What is the underlying methodology and tools?

- How should it be deployed?

- Where can it be applied?

Reading material has been provided on these questions, but permit me to summarize it for you and then let you self assess yourselves on your understanding of the concept.

As you already know, a key aspect of the Six Sigma strategy is the DMAIC methodology, a scientific/disciplined approach to problem/solving, which includes the following steps or phases…define, measure, analyze, improve, and control.  Each of these steps, which are summarized below requires a fundamental understanding of the business process being investigated.

Define.  Define and collect facts regarding a problem or opportunity.  This requires first understanding customer needs (critical to customer requirements) and their relative importance, and translating these needs into critical organizational requirements (critical to quality requirements).

Measure.  Develop process input and output measures/metrics that will enable a process owner to understand, monitor, and improve the performance of a process.

Analyze.  Establish relationships between process inputs and outputs to determine most causes; identify opportunities as well as develop a strategy and prioritization for process improvement.

Improve.  Generate, select, and implement process improvements, as well as assess their impact on process performance and customer satisfaction.

Control.  Institutionalize improvement, monitor appropriate process inputs and outputs, to ensure process gain is sustained.

Each of these phases and their associated tools will be elaborated upon in detail subsequently, as you apply the DMAIC process.”

What is Six Sigma?

Oakley continued, “Six Sigma has several facets.  It is:  (a) a business strategy, (b) a measurement, and (c) a problem prevention or problem solving process.  Sigma is a letter in the Greek alphabet.  As a strategy, Six Sigma is a data-driven philosophy and process resulting in paradigm shifts in the way a company behaves, treats its customers, and produces its products or provides its services.  From a measurement perspective, sigma is defined as the standard deviation, which is a measure of the variation of a process.  For a business or manufacturing process, the sigma value is a metric that reveals how well the process is performing.  It’s a measure of how many defects or failures are likely to occur per million opportunities.  The higher the sigma value of a process, the fewer the defects.  Thus it measures the capability of a process to perform defect-free work, where a defect can be defined as anything that results in customer dissatisfaction.  The average product or process defect rate at most major companies hovers around four sigma, or more than 6,000 defects per million (dpm) (63 dpm if process is centered).  At the Six Sigma level, by contrast, the expectation is just 3.4 dpm (2 dpb, defects per billion if process is centered).  Establishing a goal of Six Sigma would be a huge leap forward for NACE, indeed for any company.

Lastly, it is a problem prevention/problem solving process for achieving the goal.  It involves the following five steps, which we have already stated and will be elaborated upon later…define, measure, analyze, improve, and control.

As a measurement, the Sigma of a process can be easily related to dpm, assuming the process is normally distributed.  This can be determined using Excel or Minitab, assuming the specifications are known.  For example, Figure 1, shows the relationship between the short-term (centered) and long-term (1.5 Sigma shift) sigma of a process and dpm.

As a problem prevention/problem solving process, the idea is to reduce variation in our processes/products.

Why Do It?

“So what,” Jack Mitchell, the in-resident design engineer blurted out.  Oakley responded, “Variation reduction in our processes/products leads to (a) improved quality (e.g., higher yields, lower dpm), (b) lower cost (e.g., reduction in the cost of poor quality), (c) improved productivity (shorter cycle times) and (d) increased capacity.  In sum, the goals of Six Sigma are (a) the improvement of process capability and (b) the elimination of waste.

Process capability measures the ability of a process to conform to specifications.  The less variation in a process, the greater its ability to meet specifications.  Hence, we say it has a higher process capability.  In concept, process capability is the ratio of the specification range (for two-specification limits)…upper specification limit (USL) minus lower specification limit (LSL)…divided by the process variation, i.e.,

Process Capability =  What the Customer Wants =	USL-LSL

What the Customer Gets       Process Variation

Note that the lower the process variation, the greater the process capability.  This results in lower dpm, since there is a smaller chance of the output from a process exceeding the specification limits. There are precise metrics for measuring process capability, which we shall explore later (e.g., a process capability index is Cp = (USL-LSL)/6( where ( is the process standard deviation.  The Sigma of a process can then be determined by multiplying Cp by 3.  This can be converted to dpm if the process distribution is known.

Improvement in process capability and waste reduction are correlated.  Namely, if process capability increases, then dpm decreases, which results in less rework and scrap.  Rework can be viewed as waste, in the sense that it really would be virtually unnecessary (non-value added) if process quality was high.  Things would be done right the first time.  Hence, rework can be viewed as a ‘hidden factory’ within a factory, which needs to be minimized.  Moreover, process capability and cycle time are also correlated; namely, higher quality translates into lower cycle time, since rework and scrap would be reduced or eliminated.  Hence, extra work or over production would be unnecessary to meet a customer order.

In sum, Six Sigma is about (a) satisfying customers…by providing product, transactional, and service quality and on-time delivery; (b) making money…eliminating waste, inventory, delays, i.e., non-value added activities…everywhere.  To comprehend the magnitude of potential savings, the cost of poor quality for a typical company is 15-25% of sales.  For General Electric, this presented a $4 billion dollar annual savings opportunity at the time they embarked on its Six Sigma strategy.

To make sure we all understand the relationship between the sigma of a process, process capability, and dpm let’s do an exercise (Exercise 1).”

Macro & Micro Economics of Quality

“Let’s now turn our attention to money,” Oakley stated.  “More importantly, at this point, it would be useful to attempt to quantify the Cost of Quality (COQ), both from a macroeconomic and microeconomic perspective.”

Macroeconomics of Quality

“We begin by raising and attempting to answer the three following issues:  (1) Why estimate the COQ? (2) Do you know that quality costs are a greater than those that are readily identifiable (Iceberg Principle)? (3) What are the gains to be made if measured quality losses were cut in half?

I’ve summarized the answer to issue 1 (Figure 2).  The answer to issue 2 can be determined by making a list of the measured versus unmeasured costs associated with poor quality.  I have made such a listing for you (Figure 3).  Observe how much more hidden or unmeasured costs there are to measured costs.  In fact, the actual COQ has been estimated to be 6 to 50 times the measured cost.  We call this the Iceberg Multiplier.  I have also provided an example of the COQ of a major consumer electronics firm and indicated the dollar savings if measured quality costs were cut in half (Figure 4).  The average savings ($168 million) turns out to be more than their estimated earnings ($125 million), i.e.

Average Savings = (6 + 50) x $6 million

2

= $168 million

Estimated Earnings = $125 million.

For purposes of practice, let’s do an exercise on this (Exercise 2).”

Microeconomics of Quality

“The microeconomics of quality takes things down to the process level and focuses on variation and bias,” Oakley continued.” To see how this works we first need to state the components of quality at the operating level:

- Performance measure (Y)

- Performance target (T)

- Process mean (()

- Process variation ((  )

- Expected COQ (E(Y-T)2)

Quality Cost is defined as some constant times the square of the difference between the performance measure (Y) and the target (T); i.e. k(Y-T)2 .  Namely, the further the process output is from the target, the COQ increases not linearly, but as the square of the deviation from target.  The expected COQ (viz, average cost of quality) turns out to be the following:

E (COQ) = k * ((2 + (( - T)2 )

where

(2 = process variance

(( - T)2 = bias

k = constant, which is unique to a given product/process.

In general, it is unnecessary to determine k if one focuses on relative financial improvement, since the k’s would cancel.  To illustrate the computations, consider a process whose average cost per unit = $100, (2 = 9, ( = 90, and T = 100.  The E(COQ) = k* (9+102 ) = 109 * k.  If the process variance was reduced to 1, then E(COQ) = 100*k.  The E(COQ) improvement would thus be

(109-100)/109 = 8.26%.”

Let’s now do an exercise to determine the COQ for variance processes (Exercise 5).”

Getting to Six Sigma

“How can a company such as NACE get to Six Sigma?”  Sarah Miller, the equipment and facilities engineer asked.  Charles Oakley responded, “To answer this question we need to address the following:

- Where does industry stand?

- Where does NACE stand?

- Strategies that don’t work…clinging to old habits

- Changing habits

- A strategy that does work

Let’s examine each in turn.”

Where does industry stand?  Oakley pointed to a figure that depicts dpm as a function of Sigma for various types of industrial processes (Figure 5).  It also shows the Sigma of the average company.  Clearly, the team agreed, there is much room for improvement.

Where does NACE stand?  Embarrasingly, no one at NACE knew specifically.  Processes were not being measured and monitored to the extent they should be.  Everyone had a different answer, but none had any facts.  However, on one thing they did agree.  Quality was not at all the level it should be and that processes needed to be measured and monitored.  “We need to become a fact-based organization; approach things scientifically.  We also must change our mindset…think in terms of dpm, not in terms of % defectives or defects.  Two percent defective is 20,000 dpm!  Behaviorally, I might accept 2% defectives as reasonable, but 20,000 dpm, no way?”

Strategies that don’t work…clinging to old habits.  Oakley continued, “Let’s talk about our habitual ways of doing things at NACE.  In fact, let me state two examples of traditional strategies we continue to use that don’t work, which we shall later illustrate with exercises.  These are (a) using inspection (defect detection) as the primary means of controlling quality and (b) driving processes through numbers.  Inspection is now recognized as a costly and ineffective means for controlling quality.  Moreover, it doesn’t get at the root cause of the problem.  There are other drawbacks as well which we shall illustrate with an exercise (Exercise 4 and Exhibit 1).

The second example is driving processes by recent performance by putting pressure on operations to improve.  Such tactics can be highly counterproductive and violate many of Deming’s 14 principles of management.  Again, we shall illustrate this with an exercise (Exercise 5 and Exhibits 2 & 3).”

Changing habits.  As Oakley mentioned earlier, “Six Sigma is a data-driven philosophy and process resulting in paradigm shifts in the way a company behaves, treats its customers, and produces its products or provides its services.  This requires changing traditional beliefs and habits of an organization and its people.  But as we all know, we are creatures of habit and therefore, changing habitual patterns of behavior is difficult.  We shall illustrate this with an exercise (Exercise 6).

A strategy that does work.  Oakley’s final though was, “If GE and other companies have been successful using the Six Sigma strategy of DMAIC, why can’t NACE be?”  The team enthusiastically agreed and was anxious to get started.

Six Sigma Deployment

Peter Park, the factory technician then asked, “How should Six Sigma be employed?”  Charles Oakley responded, it is somewhat difficult to definitize how Six Sigma should be employed in an organization, because it is often customized to its needs.  However, there are key aspects and success factors that can be stated:

- Emphasis on statistical science and measurement.

- Rigorous and structured training deployment plans (e.g., Champion, Master Black Belt, Green Belt)

- Project-focused approach with a single set of problem prevention/solving strategies (DMAIC) and tools.

- Reinforcement of quality guru (Deming, Juran) tenets (top management leadership and support, continuous training and education, annual savings plan).

- Incorporation of Six Sigma across the entire enterprise

Since Six Sigma is a major enterprise commitment, a key factor in gaining support for its deployment and success is to develop a business plan.  This provides a roadmap of the objectives, implementation process, benefits, risks, and resource commitments over a planning horizon.  I’ve provided you with a format for a Written Business Plan (Appendix 2).

Where Can Six Sigma be Applied?

Oakley continued, “Simply put, Six Sigma can be and has been applied to essentially every business process or function (Figure 6).  An illustration of several applications are given in an article by Thomas Bysdek in the August 2001 issue of Quality Digest (Figure 7).  Transactional processes are your choice of NACE’s Order Management Process as the focus of your Six Sigma application is a good one.”

##### Exercises

# Exercise 1:  Sigma, Process Capability, DPM

What is the relationship between the Sigma of a process, process capability, and dpm?  As an illustration, assume that a process is normally distributed.  The lower and upper specification limits are LSL=2 and USL=5.  The variation in the process as measured by the standard deviation is 2 and the process is centered.  Determine process capability Cp, Sigma of the process, and dpm.  If the process standard deviation was equal to 1, what would be the process capability, Sigma of the process, and dpm?  Contrast and discuss the differences in the results obtained with the two process variations.  What are the operational and financial implications?

Exercise 2:  Macro Economics of Quality

Consider the data below.  Complete the missing information.  What would be dollar savings if we could cut scrap in half?

  - Units Sold						6 million

  - Estimated Revenues (6 x $50 per unit)		$300 million

  - Estimated Earnings (5.4% of sales)		$16.2 million

  - Scrap (Measured)					$1.875 million

  - Total Cost of Quality (Measured & Hidden)	___________

  - Total Cost of Quality (M+H) per Unit Sold	___________

  - % Total Cost of Quality per Unit/Selling Price	___________

What if we cut scrap in half?

- Savings					___________

Exercise 3:  Microeconomics of Quality

Below is a set of processes whose means ( and variances (2 vary as shown.  The target setting for the process output is T=100.  Compare the COQ’s of these processes on a relative basis.

| Process | ( | (2 | COQ |
| --- | --- | --- | --- |
| A | 90 | 9 |  |
| B | 100 | 9 |  |
| C | 90 | 1 |  |
| D | 100 | 1 |  |

Write a brief report on your analysis and state the implications of your findings.

Exercise 4:  How far can inspection get us to Six Sigma?

Task:  Count the number of times the 6th letter of the alphabet (F) appears in the text of Exhibit 1.  You have 30 seconds to perform this exercise.

Questions:

- Based (in part) on the exercise results, what is wrong with using inspection…defect detection…as the primary means of controlling and improving quality?

- What would be a better way for controlling and improving quality? Why?

- What is the impact of added inspection on quality?  For example, if the likelihood of detecting a defect is 90%, how many consecutive inspectors with this level of capability would it take to achieve a Six Sigma level of quality?  Again, what is wrong with taking such a strategy?

Exhibit 1:  Getting to Six Sigma Via Inspection

The Inspection Exercise

Task:  Count the number of times the 6th letter of the alphabet appears in the following text.

Exercise 5:  Driving Processes Through the Numbers

A company, which makes widgets is concerned about inventory levels at one of its plants.  The plant manager is under pressure to keep his inventory levels as low as possible.  In Exhibit 2 is presented a profile of inventory levels over a period from April 1994 to June 1995, with comments and actions by the plant manager.

Questions:

- What is wrong with this scenario relative to Deming’s 14 management principles (Exhibit 3).

- What is wrong with the way the plant manager is using data?  Do you have any suggestions that would help him analyze what is going on?  What role does variation play?

Exhibit 2:  Managing In-Process Inventory

- April 1994:

The in-process inventory is at a three-year low of 15.

- Manager presents an award to Dept. 50 in honor of this achievement.

- Ceremony in the cafeteria:  pizza and refreshments for all!

- “Everyone should be proud of what you’ve accomplished”.

July 1994:  Three consecutive months of inventory increases.

- Manager wishes he could take back the award.

- “Recognition seems to have been backfired.”

- Instead of holding the gains, Dept. 50 seems to have gotten complacent – allowing inventory to creep back to where it was previously.

- Manager decides:  “This group just needs tough management!”

Nov. 1994:  In-process inventory rises to a value of 26!

- Manager decides to kick anatomy and take names.

- He calls everyone in and demands they do something to keep inventories down.

- Following this tantrum, everyone in Dept. 50 treads lightly.  Short of hiding material in the dark corners of the plant, they don’t know what to do.

- So, they hold their breath and hope inventories drop.

June 1995:

- Manager has seen reduced levels of inventory since the end of last year.  “Things are looking-up!” (Although nothing had been done to change the system)

- His learning:  “Tough management style gets results!”

Exhibit 3:  Deming’s 14 Principles of Management

Exercise 6:  Changing Habits

Six Sigma is a data-driven philosophy and process resulting in paradigm shifts in the way a company behaves, treats its customers, and produces its products.  This requires changing beliefs and habits of an organization and its people.  But, as we all know, changing habitual patterns of behavior is difficult.  We shall illustrate this with a simple experiment, which was conceived by industrial engineering pioneers Frank and Lillian Gilbreth.  These have been used to train managers and college students in the principles of continuous improvement.

Task 1:  Habit

- Ask a group to divide itself into pairs (two person teams).

- Give each pair 15 blank cards.

- Ask one person in each pair to write the words continuous improvement 15 times, each time on a fresh card without looking at the previous card, and the other person to time how long it takes to write each card, as well as to record the number of errors.

Task 2:  Process Simplication…Reengineering 1

- Begin by saying to the group, “Now I am going to simplify your work by reducing your workload in half.”

- Give each pair 15 new blank cards.

- Ask the same person in each pair to write the words continuous improvement 15 times, but this time leaving out alternate letters.  Namely, write the first letter but not the second, then the third letter but not the fourth, and so on. Ensure that the person timing the experiment removes each card from the writer’s view as soon as it is written to avoid copying from a previous card.  The other person also records the time it takes to write each card as well as the number of errors.

Task 3:  Process Simplification and Modification…Reengineering 2

- “This time your work will not only be simplified, but its flow will be rearranged.”

- Give each pair 15 blank cards.

- Ask the same person to write the words continuous improvement backwards, as well as leaving out alternate letters.  (The two words must be written from left to right.  As before, the writer’s partner times each cycle, records the number of errors, and prevents the writer copying from previous cards.  In addition, the instructor should put a little pressure on the writers with comments like, “You’d better get it right, “ and “Don’t produce any defects.”

Task 4:  Imitation/Learning Actively

- After about four or five tries in Task 3, provide each writer with a template, which correctly spells continuous improvement backwards leaving out alternative letters.

- The writer’s partner again records the cycle time and number of errors.

Questions

- What are your observations and findings in Task 1?

- What are your initial observations and findings in Task 2?  How do they change over time?  What behavioral and managerial lessons can be gleaned from this task?

- What are your observations and findings in Task 3?  Contrast these with respect to Task 2 in terms of the learning curve.

- What are your observations and findings in Task 4?  What are the managerial lessons?

## Figure 1:  Six Sigma – Goal

Sigma is a statistical unit of measure that reflects process capability.  The sigma scale of measure is perfectly correlated to such characteristics as defects-per-unit, parts-per million defective, and the probability of failure/error.

Six Sigma corresponds to 2 parts per billion if process is centered.

Figure 2:  Why Estimate Cost of Quality?

- Quantify the Cost of Quality for the Business

  - Identify magnitude of potential savings

  - Sensitize Management to the size of the opportunity

  - Help to re-expose problems we have learned to tolerate

- Identify the Highest Loss Areas

- Permit Prioritizing the Loss Areas for Corrective Action

#### Figure 3a:  Measured and Hidden Costs of Quality

(Iceberg Principle)

Figure 3b: Cost of Quality Failures Worksheet

| Failure Cost Categories | Estimated Annual Costs |
| --- | --- |
| Measured Cost of Quality |  |
| Internal |  |
| Waste, Scrap | ___________________ |
| Rework | ___________________ |
| Reinspect | ___________________ |
| External |  |
| Warranties | ___________________ |
| Guarantees | ___________________ |
| Concessions | ___________________ |
| Hidden Cost of Quality |  |
| Internal |  |
| Troubleshooting and failure analysis | ___________________ |
| Evaluation to determine usability of off specification material | ___________________ |
| Engineering changes, redesign, buy-offs | ___________________ |
| Costs of reviewing quality problems (i.e., replanning, meetings, expediting, firefighting, reports, etc.) | ___________________ |
| Inventory costs on held material | ___________________ |
| Overtime because of quality problems | ___________________ |
| Late shipment premiums (delayed collections) | ___________________ |
| Material handling | ___________________ |
| Tool & fixture redesign | ___________________ |
| Machine wear | ___________________ |
| Fringe benefits on labor | ___________________ |
| Loss of productivity due to rework, scrap | ___________________ |
| External |  |
| Loss of market share due to poor quality reputation | ___________________ |
| Loss of profitability | ___________________ |
| Loss of bond credit rating | ___________________ |
| Other | ___________________ |
|  | ___________________ |
|  | ___________________ |
|  | ___________________ |

Total Hidden		___________________

Grand Total		___________________

Figure 4:  Economics of Quality – Example 1

| TV Units Sold | 5 million |
| --- | --- |
| Estimated Revenues (5 x $500 per set) | $2.5 billion |
| Estimated Earnings (5% of sales) | $125 million |
| Scrap (Measured) | $12 million |
| Total Cost of Quality (Measured & Hidden) | $72-600 million |
| Cost of Scrap per TV (12M/5M) | $2.40 per unit |
| Total Cost of Quality (M+H) per TV Sold (6/1 to 50/1 Iceberg) | $14.40 - $120 |
| % Total Cost of Quality per TV/Selling Price (14.40/500 – 120/500) | 3% - 24% |
| What if we could cut losses in half? |  |
| ½ x $12,000,000 | $6,000,000 |
| If Iceberg is between 6/1 to 50/1 | $36,000,000 to $300,000,000 |
| Recall: Total net earnings were? | $125 million |

Figure 5:  Where does U.S. Industry stand?

Figure 6.  Six Sigma Can Be Applied To Every Business Function

Figure 7:  Six Sigma and Beyond