COM4500

Software Text based Interface Specification

For Winser32.Exe V7.xx

Document Change Log

| Date | Release | Author | Comments |
| --- | --- | --- | --- |
| 22-09-2003 | 7.0 | TJ | First edition Com4500 V7.0 |
| 28-10-2003 | 7.01 | TJ | Description for text commands |
| 10-11-2003 | 7.02 | TJ | Simplifying text commands from master to WINSER32.Exe |
| 08-10-2004 | 7.03 | TJ | HOOK command with Timeouts, and NOKEY supported |
| 17-11-2004 | 7.04 | TJ | Winser32 V7.10c Rack number supported for TE1040 and CB4200 connect |
| 06-12-2004 | 7.05 | TJ | SYSADMIN, SYSCMD, Com52, TE1040, Fault command, and response structure has changed from 255 char to 512 char |
| 03-01-2005 | 7.06 | TJ | Dummy values for extended Status described |
| 03-02-2005 | 7.07 | TJ | MPT TX lever can be adjusted to -10, -13 or -16 -10dBm is default Keep Alive timer loaded if <> 0 |
| 07-03-2005 | 7.08 | TJ | Command changed Ringing on module changed from CALL to RING Ringing on emergency module changed from CALL-EMERG to RING-EMERG |
| 09-03-2005 | 7.09 | TJ | New command GPSI (Immediate GPS information – from TETRA mobile) GPST (Tricked GPS information – from TETRA mobile) GPSU (Unsolicited GPS information – from TETRA mobile) |
| 18-03-2005 | 7.10 | TJ | MPT1343 commands changed MPT1343 commands uses SYSCMD request and response |
| 24-06-2005 | 7.11 | LD+TJ | Updated GPS and VIU support Old mode KEYWORDS separated by comma KEYWORDS separated by semicolon or comma for backwards capability Please use: KEYWORDS separated by semicolon more Parameters separated by comma KEYWORD1=Param1,Param2;KEYWORD2=Param1; Winser32.exe V7.12 or higher |
| 10-11-2005 | 7.12 | TJ | P45453.ini CloseTime= n x 100 ms default (20 x 100 ms) delayed shutdown n= 0 Shutdown without delay |
| 25-05-2006 | 7.12-1 | TJ | Call frame for emergency receivers support up to 40 digits. ( Norwegian emergency receivers. Winser32.exe V7.12f or higher) |
| 28-06-2006 | 7.13 | TJ | ID from master not supported in text mode (Asciiprotocol=1) Only supported in old mode (Asciiprotocol=0) Winser32.exe V7.13 or higher |
| 31-07-2006 | 7.13-1 | TJ | COM53 and SPEEDA commands supported in document |
| 24-08-2006 | 7.15 | TJ | Support for tone TX hardware buffer full on module |
| 22-10-2007 | 7.16 | TJ | Support for MSG=SYS-EMERGENCY On emergency receiver HM807/2 or HM807/3 |
|  | 7.17 –a to h |  |  |
| 03-04-2008 | 7.18 | TJ | Support for no hardware racks P45453.ini NoRacks=1 |

| Date | Release | Author | Comments |
| --- | --- | --- | --- |
| 08-08-2008 | 7.22 | TJ | Support for ISDN A-number. MSG=SYS-CON; TYPE=HOOK; TMOD=5; DIAL=DTMF,123;ANUM=456 |
| 25-08-2008 | 7.23 | LD | Support for Tetra BaseServiceIndication |
| 23-10-2008 | 7.24 | LD | Added diversety channel reference information (FCH) |
| 25-11-2008 | 7.25 | TJ | RSSI added to COM53 frame to application server |
| 27-03-2009 | 7.30 | TJ | WinserCorba32.exe V7.30 or higher CORBA Support Winser32.exe V7.30 or higher no CORBA support |
| 20-05-2009 | ?.?? | MSA | Support for TE10-39/3 |

# Table of Contents

1	Table of Contents	5

2	Introduction	10

3	Environment	10

3.1	Overview	10

3.2	Hardware environment	11

3.3	Software environment	12

4	Transport interface Master Control - COM4500	12

4.1	Transport Protocol for data transfer (COM4500 - Master control)	12

4.2	Establishing transport connection:	12

4.3	Data Transfer	13

4.4	Closing TCPIP transport connection	13

4.5	Keep Alive:	13

5	Message interfaces	13

5.1	Common definitions for all messages	13

5.1.1	Basic Data types	13

5.1.2	Message codes and their values	17

5.1.3	Correlating requests and responses (Message Number)	19

5.1.4	Result codes	20

6	Format for message header	21

7	Administrative messages	22

7.1	Keep alive message and response	22

7.2	SYS-ADMIN command (Winser <-> App-server)	22

7.3	SYS ADMIN Command.	23

7.4	Logon	23

7.5	Reset	23

7.6	Reset OK	23

7.7	Reset Com4500	24

7.8	Set Time	24

7.9	SYS ADMIN Response.	24

8	Status	25

8.1.1	STATUS REQ	25

8.1.2	STATUS response	25

9	Extended support for 2 Com4500 system with interlink connections	27

10	EXTENDED STATUS	28

10.1.1	EXTENDED STATUS response	28

11	Conversations	31

11.1	Request total conversation information.	31

11.1.1	CONVREQ response	31

11.2	Total conversation information.	32

11.2.1	Conversation structure:	32

11.2.2	Subscriber structure:	33

11.2.3	CONVREQ response	33

11.3	Save conversation request.	35

11.3.1	Conversation response	35

12	Diversity	36

12.1	Diversity Limitations.	36

12.2	Co Channel Limitations.	36

12.3	General Diversity & Co Channel Limitations.	36

12.4	Set diversity setup	37

12.4.1	SET DIVERSITY REQ.	37

12.4.2	SET DIVERSITY Response.	40

12.5	Get diversity setup	41

12.5.1	Get DIVERSITY REQ.	41

12.5.2	GET DIVERSITY Response.	42

13	Com52 input / output	43

13.1	Com52 IO.	43

13.2	Com52 IO Response.	43

13.3	Output Command format:	44

13.4	Get input Command format:	44

13.5	Input Command format:	44

14	FAULTCMD	45

14.1	Fault CMD.	45

15	TE1040/TE1039/CB4200 CMD	46

15.1	TE1040, TE1039 and CB4200  CMD.	46

15.2	TE10-40 and TE10-39/3 Box command	46

15.2.1	CONNECT from Com4500 to master application	46

15.2.2	Matrix command from master application to Com4500	47

15.2.3	AGC command from master application to Com4500	49

15.2.4	FLASHSETUP command from master application to Com4500	49

15.2.5	Output command from master application to Com4500	50

15.2.6	Input command from Com4500 to master application	50

15.2.7	Level command from master application to Com4500	51

15.3	TE10-39/3 Box command	52

15.3.1	Display command from master application to Com4500	52

15.3.2	Key command from Com4500 to master application	54

15.3.3	Led command from master application to Com4500	55

15.3.4	Attention command from master application to Com4500	56

15.3.5	Setup from master application to Com4500	57

15.4	CB4200 Box command	59

15.4.1	CB-CONNECT from Com4500 to master application	59

15.4.2	CB-Display:    Display control	59

15.4.3	CB-Led:     Led control	62

15.4.4	CB-Attention:    Attention tone	63

15.4.5	CB-SETUP:    Setup	64

15.4.6	CB-Key:     Input from keyboard	66

15.5	TE1040 CMD Response.	67

16	MPT1343  Command format.	68

16.1	Control channel Limitations.	68

16.2	Traffic channel Limitations.	68

16.3	Command Limitations.	68

16.4	MSG command Application Server(master) -> Com4500-TSC:	69

16.5	MSG command Com4500-TSC -> Application Server (master):	69

16.6	Default setup before using MPT1343	70

16.7	Command syntax	70

16.8	Command format:	71

16.9	Command from Application Server (master)	72

16.9.1	CALL	72

16.9.2	STATUS, x	72

16.9.3	DATA, text	72

16.9.4	CLEAR	73

16.9.5	GTC	73

16.9.6	ACK,8185	73

16.9.7	ACK	73

16.9.8	ACK2	73

16.9.9	ACKB	73

16.9.10	ACKI	73

16.9.11	ACKV	73

16.9.12	ACKX	73

16.9.13	ACKX,8185	74

16.10	Command from Com4500-TSC	75

16.10.1	REG,8185	75

16.10.2	CALL	75

16.10.3	CALL, x	75

16.10.4	EMERGENCY	76

16.10.5	EMERGENCY, x	76

16.10.6	CANCEL	76

16.10.7	CANCEL, x	76

16.10.8	CON	76

16.10.9	PRESSEL	76

16.10.10	ACK specification:	77

16.10.11	Other examples	77

16.10.12	GET SETUP	77

16.10.13	SET SETUP	78

17	FMS command format for COM4500-TSC	82

17.1	Channel Limitations.	82

17.2	Speech connections	82

17.3	Application Server(master) -> Com4500-TSC:	82

17.4	Com4500-TSC -> Application Server (master):	82

17.5	Command format:	82

17.6	Command from Application Server (master)	83

17.6.1	STATUS	83

17.6.2	STEXT	83

17.6.3	ACK	83

17.6.4	TONEACK	83

17.6.5	TON1750	83

17.6.6	TON2135	83

17.7	Command from Com4500 to Application Server (master)	84

17.7.1	STATUS	84

17.7.2	TON1750	84

17.7.3	TON2135	84

17.8	ACK specification:	84

17.9	Set FMS setup.	87

18	SYS CMD	89

18.1	SYS CMD.	89

18.2	SYS-CON command (App-server -> Winser)	90

18.2.1	XCH support	92

18.2.2	CON-CONX section	92

18.2.3	JOIN	95

18.2.4	HOLD and PARK	95

18.2.5	HOOK	95

18.2.6	REMOVE	96

18.2.7	DISCONNECT	96

18.2.8	DISCONNECTCONFIRM	96

18.2.9	MON-XXXX section	97

18.2.10	MUTE	97

18.2.11	PLAY-XXXX	98

18.2.12	RECORD-SOUND	98

18.2.13	RECORD-STOP	98

18.3	SYS-CON command: (Winser -> App-server)	98

18.4	SYS-OUT command: (App-server ->Winser)	99

18.5	SYS-EMERGENCY command: (App-server ->Winser)	100

18.5.1	Com53 output call commands	101

18.5.2	Com53 output  commands	103

18.5.3	Com53 internet AF connection OPEN/ CLOSE  commands	103

18.5.4	SPEEDA commands	104

18.6	SYS-INP command (Winser -> App-server)	108

18.7	SYS-EMERGENCY  command: (Winser -> App-server)	109

18.8	SYS-EMERGENCY RINGING command: (Winser -> App-server)	110

18.8.1	Com53 input  commands	111

18.8.2	Com53 input Call commands	111

18.9	Tetra Call	112

18.9.1	Incoming speech call from 3317	112

18.9.2	Outgoing speech call to 3317	112

18.9.3	Outgoing text call to 3317	112

18.9.4	Incoming text call from 3317	113

18.9.5	Incoming status call as text  from 3317	113

18.9.6	Group setup to 3316 (local tetra connected to VIU unit)	113

18.9.7	Get Immediate GPS Request from 331)	114

18.9.8	Setup Triggered GPS on 3317	114

18.9.9	Unsolicited GPS information from 3317	114

18.9.10	Tetra BaseServiceIndication	114

18.10	SYS CMD Response.	114

19	SYS ICCS	115

19.1	SYS ICCS	115

19.2	ICCS-CMD  /  ICCS-RSP commatext format	115

19.3	Registration functions/responses	116

19.4	API Function: McdiRegisterClientEx	116

19.5	API Function: McdiDeRegisterClient	116

19.6	API Response: McdiClientRegistrationStatus	116

19.7	AssignResource functions/responses	117

19.8	API Function: McaAssignResourceEx	117

19.9	API Function: McaDeassignResource	117

19.10	API Response: McaAssignmentStatus	117

19.11	API Response: McaAssignResourceError	118

19.12	API Response: McaAssignResourceWarning	119

19.13	API Response: McaDeassignResourceError	119

19.14	API Response: McaDeassignResourceWarning	119

19.15	PrivateCall functions/responses	120

19.16	API Response: McaPrivateCallStatus	120

19.17	API Function: McaBeginPrivateCall	120

19.18	API Function: McaAnswerPrivateCall	120

19.19	API Function: McaEndPrivateCall	121

19.20	API Function: McaRejectPrivateCall	121

19.21	API Response: McaBeginPrivateCallError	122

19.22	API Response: McaAnswerPrivateCallError	122

19.23	API Response: McaRejectPrivateCallError	123

19.24	API Response: McaEndPrivateCallError	123

19.25	EmergencyCall functions/responses	124

19.26	API Response: McaEmergencyCallStatus	124

19.27	API Response: McaEmergencyAlarmStatus	124

19.28	API Function: McaAcknowledgeEmergency	125

19.29	API Response: McaAcknowledgeEmergencyError	125

19.30	API Function: McaEndEmergency	125

19.31	API Response: McaEndEmergencyError	126

19.32	API Response: McaBeginConsoleEmergencyCallError	126

19.33	Select/DeselectResource (talk group) functions/responses	127

19.34	API Function: McaSelectResource	127

19.35	API Response: McaSelectResourceError	127

19.36	API Function: McaDeSelectResource	127

19.37	API Response: McaDeSelectResourceError	128

19.38	API Response: McaResourceSelectStatus	128

19.39	API Response: McaResourceStatus	128

19.40	API Response: McaCriticalResourceStatus	129

19.41	Inbound Call responses	130

19.42	API Response: McaInboundRadioStatus	130

19.43	API Response: McaInboundPrivateCallStatus	130

19.44	API Response: McaInboundCallStatus	131

19.45	API Response: McaInboundPttIdStatus	131

19.46	Volume Control  functions/responses	132

19.47	API Function: McaChangeVolume	132

19.48	API Response: McaResourceVolumeStatus	132

19.49	API Response: McaChangeVolumeError	132

19.50	Transmit  functions/responses	133

19.51	API Function: McaBeginInstantTransmit	133

19.52	API Response: McaBeginInstantTransmitError	133

19.53	API Function: McaEndInstantTransmit	133

19.54	API Response: McaEndInstantTransmitError	134

19.55	API Response: McaResourceTransmitStatus	134

19.56	API Response: McaGeneralTransmitStatus	134

19.57	McdbGetOpId  functions/responses	135

19.58	API Function: McdbGetOpId	135

19.59	API Response: McdbGetOpIdResponse	135

19.60	API Response: McdbGetOpIdError	135

19.61	API Response: OperProcessStatus	136

20	Emergency receiver HM674/8	138

20.1	CALL_EMERG – DTMF digit format GSM Phone Alarm:	139

20.2	SCANCOM Alarm	141

20.3	Lift Alarm	142

20.4	Beach Alarm	143

20.5	Protocol error Alarm	144

# Introduction

This document gives an overview of the interface functions supported by the communication protocol and a typical message sequence. The message format, socket port number, protocol state machine, error recovery details are given to the level of detail sufficient for programming the interface.

# Environment

Please note following!

P45453.Ini

[WinServ]

Asciiprotocol=1

1= text based input and text based output commands.

Use this document Com4500_CTI07-xx-Text.DOC

0= old input and output commands.

Use document Com4500_CTI07-xx.DOC

## Overview

The diagram below illustrates the interface between COM4500 and the master control. Calls are received on the modules of COM4500 and sent to the master control. When the master control is ready to accept the call, the master control will request COM4500 to set-up audio connection.

## Hardware environment

The COM4500 hardware consists of NT, 2000 or XP Workstation for the software and a number of 19” racks containing interface modules to the “World”. A rack can be a single or double unit. A single or a double unit has one RS232 interface connection to the Workstation. The number of modules and the load on the system determents the actual number of rack units that can be use.

## Software environment

COM4500 implements the software solution on a Windows NT, 2000 or XP operating system using TCP/IP protocol for Software component interaction.

.

The COM4500 software consists of a set-up program and the running software called Winser32.

The set-up program configures the actual modules, the ports and names for TCP/IP protocol.

The Winser32 load the configuration during start-up and runs the hardware and software interface.

# Transport interface Master Control - COM4500

All commands, responses, signal events are exchanged between the master control and COM 4500 using TCP-IP PROTOCOL as described below.

The principle is based on a command with a message number and a response for that command returning the message number. Each subscriber (module) based command can have up 10 outstanding responses. The receiver of the command (application server - master control) have to answer  each command.

Environment variable in P45453.INI can prevent responses to application server (master control) for some commands. If the commands are not accepted you will get responses.

## Transport Protocol for data transfer (COM4500 - Master control)

TCP/IP connection oriented interface is used for exchanging commands, events etc. The master control will listen for connections and COM4500 will establish a primary or a secondary connection on ether one master control or two different controls on the system. If the primary connection disconnect or fails, the COM4500 will reset all its modules to their standby positions and try to connect to the secondary connection. When the primary connection is re-established the COM4500 will reset all its modules to their standby positions and disconnect the secondary connection and use the primary connection for communication.

The port numbers for listening to connection is XXXXXX. The port numbers is retrieved from services using socket API or any other means with out having to re-program the master control or COM 4500.  The Service names can be any name.

## Establishing transport connection:

The master control / controls will listen for connections on predefined TCP-IP-ports and accept calls on specified ports. COM4500 will start using the primary connecting. If the connection fails it will try connecting to the secondary connection. If the primary connection is lost then COM4500 will retry connection every 10-sec.

If the primary and the secondary connection are lost or fail then COM4500 will retry to connect every 10-sec on both.

## Data Transfer

Calls/Events/Error messages will be sent from COM4500 to the master control and the master control will acknowledge the messages. The master control will issue the commands to COM4500 and COM4500 will reply to the commands. The detailed message formats are described in later sections. All data are sent as normal data. Expedited messages are not used.

## Closing TCPIP transport connection

Either side can close the connection using the socket close commands.

## Keep Alive:

COM4500 will send Keep Alive message periodically to the master control on the established connection and the master control will monitor the status of the COM4500. The Keep Alive time interval is returned in the LOGON response message. If Keep Alive is not received with in (6 * Keep Alive interval) then the master control should disconnect and report an error.

# Message interfaces

All messages should have header, data. The structure for message header is the same but the actual data for each message is different. The date types, requests vs. responses, result codes, message header, and data are described in detail in the following sections.

## Common definitions for all messages

### Basic Data types

Both character and binary formats are used in the interface.

- The byte ordering of data types short, long will be as in INTEL 8086.

- The date time format will be YYYY-MM-DD:HH:MM:SS (ASCII )

- The date format will be YYYY-MM-DD (ASCII)

- The time format will be HH:MM:SS (ASCII)

Digit over the network will be ASCII for HOOKOFF, SIGNAL and CONNECT.

DTMF

0-9         = “30-39”

0A HEX  = “A”

0B HEX  = ”B”

0C HEX  = “C”

0D HEX  = “D”

0E HEX  = “*”

0F HEX  = “#”

Special characters to COM4500 from master control

“,” = Wait 1.5 sec before next digit is transmitted

“W” = Wait for dial tone before next digit is transmitted

CCIR, ZVEI

0-9         = “30-39”

0A HEX  = “A”

0B HEX  = ”B”

0C HEX  = “C”

0D HEX  = “D”

Special characters to COM4500 from master control

“L” = Next tone is transmitted in long format (CCIR = 700 ms; ZVEI = 490 ms)

“F” = No Tone

You can change following in the registration database.

HKEY_LOCAL_MASHINE -> Software -> HMortensen -> P45453 ->

PathDat			Location of data files *.dat

PathExe		Location of exe files *.exe

PathLog		Location of log files *.Log

PathVoice		Location of voice files *.wav

Language		[Dansk| Svensk| Norsk| English| German| Polish or

Danish| Swedish| Norwegian| English| German| Polish]

HeaderSystemNo	Header System number - Default = 1 (2 = Com4500 system 2)

Using 2 systems and HM806 as AF interconnections you have to

Setup system 2 (Header System No= 2 and IP address, Listen port for

HM-Server system 1 (HM network setup system 2))

Using HM806 as AF interconnections you connect all HM806

modules to a separate 100 M bit HUB. 8 racks are supported

for one system, and 2 x 4 racks for two systems.

CcirLetTime:   		Keying transmitter before tones in steps of 10 ms. – Default = 20

CcirLongTone:		Long CCIR tone in steps of 10 ms. – Default = 70

ZveiLetTime:		Keying transmitter before tones in steps of 10 ms. – Default = 14

ZveiLongTone:		Long ZVEI tone in steps of 10 ms. – Default = 49

DtmfLetTime:		Pause before starting tones in steps of 10 ms. – Default = 10

DtmfToneOn:		Tone in steps of 10 ms. – Default = 7

DtmfToneOff:		Tone pause in steps of 10 ms. – Default = 7

EiaLetTime:		Keying transmitter before tones in steps of 10 ms. – Default = 20

EiaLongTone:		Long Eia tone in steps of 10 ms. – Default = 700

EiaTone:		Eia tone in steps of 10 ms. – Default = 23

EEALetTime:		Keying transmitter before tones in steps of 10 ms. – Default = 20

EEALongTone:		Long EEA tone in steps of 10 ms. – Default = 600

EEATone:		EEA tone in steps of 10 ms. – Default = 4

LetTime625:		Keying transmitter before tones in steps of 10 ms. – Default = 15

ToneTime625:		Fms 625 Hz single tone in steps of 10 ms. – Default = 40

LetTime1750:		Keying transmitter before tones in steps of 10 ms. – Default = 15

ToneTime1750:		Fms 1750 Hz single tone in steps of 10 ms. – Default = 100

LetTime2135:		Keying transmitter before tones in steps of 10 ms. – Default = 15

ToneTime2135:		Fms 2135 Hz single tone in steps of 10 ms. – Default = 100

MptLetTime:		Keying transmitter before tones in steps of 10 ms. – Default = 16

MptLevel:		-10, -13 or -16     Default = -10dBm   (i.e. minus 13)

ServerListen:		Server listen port for rack simulator and remote server. Default= 1050

UdpServerListen:	Server UDP listen port (49160). Default:=  -1 (not active)

RelAddress:		0 = absolute address  1 = relative address

Absolute address = module number between 1 and 224.

Server and rack modules

Relative address  = module number between 1 and xxx for the server

Module number > 224 in the system forces

relative addressing

Relative address  = Rack module numbers between 1 and 64 each rack

ConfUpdate:		0 = No conversation information   1 = conversation information to

Master. Default = 0

UseAscII:		1 = digits ASCII (CCIR, ZVEI, DTMF)  1 = default

RackRetransTime	Empty use setup values for frame retransmission to rack

Value defined overwrite frame retransmission to all  racks

Using steps of 10 ms RackRetransTime =100  (100 * 10 ms = 1000 ms)

RackRetransCount	Empty use setup values for number of retransmissions to rack

Value defined overwrite number of retransmissions to all  racks

RackRetransCount =5 uses 5 retransmissions to all rack

NoAutoAlerting:	Empty = Server answer with alerting –  Auto alerting is Default

1 = Application server answer with alerting to accept a ringing

WaitToneLevel:	Empty = default -10dBm, 0 = -10dBm, 1= -12dBm, 2= -14dBm etc

IsdnBusyTime:		Empty= shutdown isdn without delay.

N x 100 ms delay shutdown indicating busy tone from subscriber.

P45453.Ini		Receiving Text based commands from Com4500 server to master

[WinServ]

Asciiprotocol=1		1= text based input commands (recommended)

0= old input commands (Com4500_CTI07-xx.DOC)

IsdnProgress=1		Transmit Isdn Progress commands from Winser to master

NoHookResponse=1		No hook response to master if command is accepted

NoKeyResponse=1		No Key response to master if command is accepted

NoRelayResponse=1		No Relay response to master if command is accepted

NoTE1040Response=1		No TE1040 / CB4200 response to master if command is accepted

X2Monitor=1			Run X2monitor on old Xmonitor commands

MaxNumberOfLogFiles= 15    Max number of log files - default= 10

MaxNumberOfIhmLogFiles= 20    Max number of Ihm internal log files - default= 10

CloseTime=			n x 100 ms close down delay default (20 x 100ms)

n= 0 close down without delay

NoSystemMenu=1                    Winser32.exe has no system exit menu

NoExitBut=1                             Winser32.exe has no  Exit button

NoExitMenu=1                         Winser32.exe has no  exit menu

### Message codes and their values

The value column specifies the request message value in decimal. The request value is even when it is a request. All request messages have response and the message code has the value of request message code plus one. The Direction column indicates the sender of the message and the receiver.

| Request | Value | Direction | Comment | Response |
| --- | --- | --- | --- | --- |
| KEEP ALIVE message | 8 | COM 4500 ( MASTER | Keep alive message from COM4500 to the master control | Keep Alive response |
| STATUS REQ | 28 | MASTER ( COM4500 | The status is returned in the response | STATUS response |
| CONVREQ | 124 | MASTER ( COM4500 | Request issued by the master Total conversation info | Conv. req. Response. |
| CONVALL | 126 | COM4500 ( MASTER | Total Conversation information. | Conv. Response. |
| Get diversity Req. Text based CMD | 132 | MASTER ( COM4500 | Get information about diversity channel | Diversity response |
| Set diversity Req. Text based CMD | 134 | MASTER ( COM4500 | Set information about diversity channel | Diversity response |
| Com52Io Text based CMD | 136 | MASTER <( COM4500 | Com52 IO command | Com52 Io response |
| Fault command Text based CMD | 138 | COM4500 ( MASTER | Fault information | No Response |
| TE1040 | 140 | MASTER <( COM4500 | TE1040 box command | TE1040 response |
| EXTSTATUSREQ | 306 | MASTER ( COM4500 | Extended The status is returned in the response | Ext STATUS response |
| SAVECONVWIN | 308 | MASTER ( COM4500 | Request to save contents of conversation window. | Conversation Response. |
|  | 310 |  |  |  |
|  | 312 |  |  |  |
|  | 314 |  |  |  |
| FMS Text based CMD | 316 | MASTER ( COM4500 COM 4500 ( MASTER | FMS command FMS command | FMS response FMS response |
| GETFMS Text based CMD | 318 | MASTER ( COM4500 | FMS get setup command | FMS get setup response |
| SETFMS Text based CMD | 320 | MASTER ( COM4500 | FMS setup command | FMS setup response |
|  | 322 |  |  |  |
|  | 324 |  |  |  |

| Request | Value | Direction | Comment | Response |
| --- | --- | --- | --- | --- |
| SYSCMD Text based CMD | 350 | MASTER ( COM4500 COM 4500 ( MASTER | Text based commands | SYSCMD Response SYSCMD Response |
| SYSADMIN Text based CMD | 352 | MASTER ( COM4500 COM 4500 ( MASTER | Text based commands | SYSADMIN Response SYSADMIN Response |
| SYSICCS Text based command | 354 |  |  |  |

### Correlating requests and responses (Message Number)

- There can be more than one outstanding request.

- In the message header, a field 'message number' is defined. The 'message number' field is set by the caller and returned in the corresponding response. The caller may use this field to correlate commands and responses. The response corresponding to the request must contain the same value as given in the request.

- The Com4500 server starts with message number 1 for logon request and increments the number for the following commands and make a wrap around at FFFF hex.

- The master control should start with  message number 1 for the first command (not response) transmitted to Com4500 after logon and increments the number for the following commands and make a wrap around at FFFF hex.

### Result codes

All messages contain a field called Result code in the header.

- The result code field has meaning only for response messages.

- The called process should return the result of the request in this field.

- A result of zero should be returned to indicate success of the request (command).

- Other result codes indicate failure of the operation.

The following error codes have been identified and their values are given below.

Error codes

0001:	General rejection code

0002:	Module occupied bye another user

0003:	Line fault on module

0004:	No response from the client / subscriber

0005:	No connection to client / subscriber

0006:	Module does not exist

0007:	No speech channels

0008:	Out of range

0010:	No tones transmitted

0011:	Command fault

0012:	One or more modules do not exist

0013:	Max number of MPT retransmissions

0014:	Unknown

0015:    MPT is busy

1000:	Module already disconnected

1003:	Module in standby position or dial tone detected

1005:	ID or module number is invalid

# Format for message header

The header format should be as described below and should be sending in the same field number order. The header have a timestamp witch can be used for logging purposes

Length of header is 50 bytes.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | SOH | Char | 4 | **** | **** | ASCII – Set this field to this value always |
| 2 | Version | Unsigned Short | 2 | 0 | 0 to 9999 | Support for version numbers from V 7.00 = 700 Version DIV 100 = Main no 7 Version MOD 100 = Sub no 00 |
| 3 | Header System number | Unsigned Short | 2 | 0 | 0 to 9999 | Header system number 0 = System 1 1 = System 1 2 = System 2 |
| 4 | Signal Time | Char | 20 | Spaces |  | ASCII – Signal time in Date time format as described earlier |
| 5 | Message Type | Unsigned Short | 2 | 0 | 0 to 9999 | Valid message type. See section message types |
| 6 | Message number | Unsigned Short | 2 | 0 |  | See description for message number above. |
| 7 | Result Code | Unsigned Short | 2 | 0 |  | See description for result code above. |
| 8 | Data Length | Unsigned Long | 4 | 0 |  | Length of data excluding the header size. For example, message with out data will have Data length zero. |
| 9 | Filler | Char | 8 | Binary 0 ('\0') |  | Initialize to binary zero and for future use. |
| 10 | EOH | Char | 4 | #### | #### | ASCII – Set this field to this value always. |

- COM4500 HEADER SYSTEM NUMBER.

COM4500 is a standalone configuration, but two or more COM4500 can work in parallel.

COM4500 uses a system number to separate the messages from each system.

# Administrative messages

## Keep alive message and response

COM4500 will send KEEP-ALIVE message periodically to the master control and the master control will monitor the status of the COM4500. The KEEP-ALIVE interval is received in the Logon message response. If KEEP-ALIVE is not received with in (5 * keep alive interval) then the master control should disconnect and report error to operators.

The KEEP-ALIVE message has only standard header

The KEEP-ALIVE response has only standard header

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3

## SYS-ADMIN command (Winser <-> App-server)

Administrative commands overview

MSG=			SYS-ADMIN

TYPE= 		[Action type]

RESET

RESETOK

RESETCOM4500

LOGON

SETTIME

FMOD=		[Module]

RACK=		x	x= 0 all rack		x=1 to 8 rack x

ERRTEXT=		Error text

RESTART=		x	x=0 start up		x=1 reconnected

KEEPALIVETIME=	x	x=10 sec. default	x > 0  then new value

TIME=			2003-09-23 12:34:01

## SYS ADMIN Command.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

MSG=Command string from SYS-ADMIN

## Logon

Logon with start up from Copm4500 to master

MSG=SYS-ADMIN;TYPE=LOGON;RESTART=0;KEEPALIVETIME=10

Response changing Keep alive timer to 15 sec.

MSG=SYS-ADMIN;TYPE=LOGON;RESTART=0;KEEPALIVETIME=15

Logon with reconnect from Copm4500 to master

MSG=SYS-ADMIN;TYPE=LOGON;RESTART=1;KEEPALIVETIME=10

Response changing Keep alive timer to 15 sec.

MSG=SYS-ADMIN;TYPE=LOGON;RESTART=1;KEEPALIVETIME=15

Response changing Keep alive timer to 2 sec.

MSG=SYS-ADMIN;TYPE=LOGON;RESTART=1;KEEPALIVETIME=2

## Reset

From Copm4500 to master

Received reset from rack 1 having modules indicated by FMOD

MSG=SYS-ADMIN;TYPE=RESET;RACK=1;FMOD=1,2,3,25,127

## Reset OK

From Copm4500 to master

Received reset OK from rack 1 having modules indicated by FMOD

MSG=SYS-ADMIN;TYPE=RESETOK;RACK=1;FMOD=1,2,3,25,127

## Reset Com4500

From master to Copm4500

Reset all Com4500 rack

MSG=SYS-ADMIN;TYPE=RESETCOM4500;RACK=0

Reset  Com4500 rack 1

MSG=SYS-ADMIN;TYPE=RESETCOM4500;RACK=2

## Set Time

From master to Copm4500

Set time on server

MSG=SYS-ADMIN;TYPE=SETTIME;TIME=2003-09-23 12:34:01

## SYS ADMIN Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Error Text | Char | 80 | Spaces |  | Text |
| 4 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

- Message

MSG=Command string from SYS-ADMIN

# Status

### STATUS REQ

The STATUS REQ message has only header.

The response returns the status.

### STATUS response

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Number of modules | Short | 2 | 0 |  | 0 = no modules 1 = module status 1 x 10 bytes 2 = module status 2 x 10 bytes |
| 2 | ID. | Unsigned Long | 4 | 0 |  | Identification number for the first module number |
| 3 | Module number | Unsigned Short | 2 |  |  | Module number for the first module. |
| 4 | Module type | Unsigned Short | 2 |  |  | MOD_ZERO = 0 MOD_CHANNEL = 1 MOD_TELEPHONE = 2 MOD_MANPHONE = 3 MOD_PABX = 4 MOD_OPERATOR = 5 MOD_AF = 6 MOD_SOUND = 7 MOD_MANBOX = 9 MOD_TAPE = 10 |
| 5 | Module Status | Unsigned Short | 2 |  |  | STAT_STANDBY = 0 STAT_BUSY = 1 STAT_DIALING = 2 STAT_CONNECT = 3 STAT_SIGNAL = 4 STAT_WAIT = 5 |
| 6 | ID. | Unsigned Long | 4 | 0 |  | Identification number for the next module number |
| 7 | Module number | Unsigned Short | 2 |  |  | Module number for the next module. |
| 8 | Module type | Unsigned Short | 2 |  |  | Module type for the next module |
| 9 | Module Status | Unsigned Short | 2 |  |  | Module status for the next module |
| Etc |  |  |  |  |  |  |

- ID.

Always zero

- MODULE NUMBER

Actual module number

- MODULE TYPE. (Module type for the module).

MOD_ZERO:		Not used

MOD_CHANNEL:		Radio module

MOD_TELEPHONE:	Normal telephone

MOD_MANPHONE:	Manual telephone

MOD_PABX:		Local PABX or public telephone line module

MOD_AF:			AF module

MOD_SOUND:		Voice module for SoundBlaster

MOD_MANBOX:		CB4200 Box

MOD_TAPE:		Custom tape

- MODULE STATUS

Actual status for the module number

STAT_STANDBY = Standby position for the module

Status <> STAT_STANDBY = module is busy

# Extended support for 2 Com4500 system with interlink connections

Both systems have module 1 to for example 150 and it is the master control that decides what modules it want to use in system 1 or 2. To support AF between the two systems you have to obtain a link index support from system A and use this link index in calls to system B.

Using 2 systems and HM806 as AF interconnections you have to Setup system 2 (SystemHeaderNo= 2 and IP address, Listen port for HM-Server system 1)

Using HM806 as AF interconnections you connect all HM806 modules to a separate 100 M bit HUB. 8 racks are supported for one system, and 2 x 4 racks for two systems.

System A is the system where your reference module is located and where you obtain link index for the system (system 1 or 2).

System B (system 1 or 2) is the other system where your reference module isn’t located and where you use the obtained link index (from system A) as reference module.

If you only communicate in system A you will not need link index support.

If you want to communicate in system A and in system B from your reference module (typically an operator) you will need link index support.

If you want to remove a link index from the system you have to do it in a two step procedure.

- First you remove all module connected to the reference link index in system B

- Then you have to remove link support from system A

If module 1 in system A want to communicate with module 150 in system A and module 10 in system B.

- Extended connect call to system A  ( from module=1, to module= 150 and Link Request = 1)

- Extended connect response receives for example (from module=1, to module= 150 and Link index = 3) (system A)

- Extended connect call to system  B  ( from module=0, Link index = 3, to module= 10 and Link Request = 0)

- Extended connect response receives(from module=0,to module = 10 and Link index = 3 (System B)

# EXTENDED STATUS

The EXTENDED STATUS REQ message has only header.

The response returns the status.

### EXTENDED STATUS response

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Number of modules | Short | 2 | 0 |  | 0 = no modules 1 = module status 1 x 62 bytes 2 = module status 2 x 62 bytes |
| 2 | ID. | Unsigned Long | 4 | 0 |  | Identification number for the first module number |
| 3 | Module number | Unsigned Short | 2 | 0 | 1 – xxx | Module number for the first module. |
| 4 | Module type | Unsigned Short | 2 | 0 |  | MOD_ZERO = 0 MOD_CHANNEL = 1 MOD_TELEPHONE = 2 MOD_MANPHONE = 3 MOD_PABX = 4 MOD_OPERATOR = 5 MOD_AF = 6 MOD_SOUND = 7 MOD_MANBOX = 9 MOD_TAPE = 10 |
| 5 | Module Type no | Unsigned Short | 2 | 0 | 1 – xxx | Module Type number |
| 6 | Module Status | Unsigned Short | 2 | 0 |  | STAT_STANDBY = 0 STAT_BUSY = 1 STAT_DIALING = 2 STAT_CONNECT = 3 STAT_SIGNAL = 4 STAT_WAIT = 5 |
| 7 | Dummy 1 | Unsigned Short | 2 | 0 |  |  |
| 8 | Dummy 2 | Unsigned Short | 2 | 0 |  |  |
| 9 | Dummy 3 | Unsigned Short | 2 | 0 |  |  |
| 10 | Dummy 4 | Unsigned Short | 2 | 0 |  |  |
| 11 | Module name | Char | 40 | Spaces |  | Text |
| 12 | Module Status | Unsigned Short | 2 | 0 |  | Module status for the next module |
| Etc |  |  |  |  |  |  |

- ID.

Always zero

- MODULE NUMBER

Actual module number

- MODULE TYPE. (Module type for the module).

MOD_ZERO:		Not used

MOD_CHANNEL:		Radio module

MOD_TELEPHONE:	Normal telephone

MOD_MANPHONE:	Manual telephone

MOD_PABX:		Local PABX or public telephone line module

MOD_AF:			AF module

MOD_SOUND:		Voice module for SoundBlaster

MOD_MANBOX:		CB4200 Box

MOD_TAPE:		Custom tape

- MODULE TYPE NO. (Module type number for the module).

- MODULE STATUS

Actual status for the module number

STAT_STANDBY = Standby position for the module

Status <> STAT_STANDBY = module is busy

- DUMMY 1

Subtype for IHM NAME . Default = 0

Only

IHM_HM808_2,

IHM_HM807_2, IHM_HM807_3

IHM_HM815_1, IHM_HM816_1, IHM_HM817_1 uses subtypes

- DUMMY 2

Mode for Module

- DUMMY3

IHM NAME

0 =  IHM_ZERO

1=   IHM_HM699_1    Io kort    8 input 8 output

2=   IHM_HM674_5    ISDN PABX

3=   IHM_HM674_7     Emergency PABX

4=   IHM_HM724_6,    Telephone   8TE Module  2 subscriber

5=   IHM_HM723_1,    Operator      8TE Module

6=   IHM_HM654_3,     Sound module

7=   IHM_HM512,        Power supply.

8=   IHM_HM580_1,    Radio module

9=   IHM_HM654_4,     Radio module

10=  IHM_HM623_1,     Operator      8TE Module

11=  IHM_HM801_3,     CPU  tone RX and TX.

12=  IHM_HM801_11,   Tone Rx and TX

13=  IHM_HM802_1,    Matrix kort

14= IHM_HM807_1,     Multikort 8 subscriber

15=  IHM_HM808_1,    Multikort 4 subscriber

16=  IHM_HM813_1,     Special module  4TE Module

17=  IHM_HM882_5,     Multi card 4 subscriber  4TE Module

18=  IHM_HM802_2,     Tape    4TE Module

19=  IHM_HM814_1,     MUX                          4TE Module

20=  IHM_HM807_2,     Multi card 8 subscriber  4TE Module

21=  IHM_HM807_3,    Multi card 2 subscriber   4TE Module

22=  IHM_HM882_7,     PABX card 1 subscriber   4TE Module

23=  IHM_HM812,        Power supply.

24=  IHM_HM803,        DSP Matrix.

25=  IHM_HM699_2,    IO card  16 input

26=  IHM_HM699_3,     IO card 16 output

27= IHM_HM806,        Matrix net link  64

28=  IHM_HM808_2,     Multi card 4 subscriber

29=  IHM_HM815_1,     Isdn-30

30=  IHM_HM816_1,     4 x PABX

31=  IHM_HM817_1      4 x   COM53 interface

- DUMMY4

Bit0 = 1 VIU Tetra unit connected to this module

# Conversations

## Request total conversation information.

This message is send, if a master needs to know which conversation is in progress.

A CONVALL is send after response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | Identification number generated by the master control |

- ID.

Always zero.

### CONVREQ response

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | Identification number generated by the master control |
| 2 | Number | Unsigned Short | 2 | 0 | 0 | Not used |
| 3 | Error text | Char | 80 | Spaces |  | Any text to describe the error. |

- ID.

Number supplied by the master control to identify further actions on the module

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

## Total conversation information.

Conversation information to master only if ConfUpdate = 1. (REG. Database)

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | ID from Req. |
| 2 | Conv | Unsigned Long | 4 | 0 | 0-255 | Number of Conversation structures. |
| 3+n | Conversation | See below | 425 x (n+1) | 0 | - | A structure describing the conversation (Conversation structure). |

- ID.

Always zero

- Conv.

Number of Conversation structures.

- Conversations.

A number of Conversation structures.

### Conversation structure:

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Up down | Unsigned char | 1 | 0 | 1 | Always 1 |
| 2 | Talk Channel | Integer | 4 | 0 | 0-255 | Conversation number |
| 3 | Conf mode | Integer | 4 | 0 | X | Mode of conversation. DSP_CLOSE = 0 DSP_CONF = 1 DSP_OPEN = 2 DSP_TALK = 3 DSP_LISTEN = 4 DSP_MONITOR = 5 DSP_MONGAIN = 6 |
| 4 | Subscriber | See below | 32 x 13 | 0 | - | 32 x structures describing the subscribers (See Subscriber structure). |

- Up down.

Used internally by COM4500. Always 1.

- Talk Channel.

A unique number identifying the individual conversations.

- Conf mode.

DSP_CLOSE	=	0	Close all.

DSP_CONF	=	1	All in conference

DSP_OPEN	=	2	Subscriber 1 talks and listen to all.

DSP_TALK	=	3	Subscriber talks with all.

DSP_LISTEN	=	4	Subscriber listen to all.

DSP_MONITOR	=	5	Subscriber monitoring all.

DSP_MONGAIN	=	6	Subscriber monitoring all with gain.

- Subscriber.

A structure describing the subscribers (See Subscriber structure).

### Subscriber structure:

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Task ID | Unsigned char | 1 | 0 | Any | Used internally by COM4500. |
| 2 | Num | Unsigned Short | 2 | 0 | 0-xxx | Module in conversation |
| 3 | Extra Subscriber | Unsigned Long | 4 |  | Any | Used internally by COM4500. |
| 4 | Extra Subscriber2 | Unsigned Long | 4 |  | Any | Used internally by COM4500. |
| 5 | Mode | Unsigned Char | 1 |  | 0-255 | Used internally by COM4500. |
| 6 | Gain | Unsigned Char | 1 |  | 0-255 | Used internally by COM4500. |

- Task ID.

Used internally by COM4500.

- Num.

Module in conversation.

- Extra Subscriber.

Used internally by COM4500.

- Extra Subscriber2.

Used internally by COM4500.

- Mode

Used internally by COM4500.

- Gain

Used internally by COM4500.

### CONVREQ response

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | Identification number generated by the master control |
| 2 | Number | Unsigned Short | 2 | 0 | 0 | Not used |
| 3 | Error text | Char | 80 | Spaces |  | Any text to describe the error. |

- ID.

Always zero

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

## Save conversation request.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | Identification number generated by the master control |
| 2 | Filename | char | 255 | 0 |  | Path+filename |

- ID.

Always zero

- Filename.

Specify the full path or just the filename or just the directory.

If no filename is specified a default filename (convsnapshot.Txt) is used.

If no directory is specified a default directory (Specified by pathlog in registry)

### Conversation response

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 |  | Identification number generated by the master control |
| 2 | Num | Unsigned Short | 2 | 0 |  | Not used |
| 3 | Error text | Char | 80 | Spaces |  | Any text to describe the error. |

- ID.

Always zero

# Diversity

Two or more modules can be grouped in a common diversity channel. A diversity channel is called by a channel reference number for the channel. This channel reference number shall be greater than the highest module number in the system (for the moment greater than 512) and less than 64000. The number is defined as the first comma separated parameter in channel setup.

The behaviour of a call to a diversity channel depends of the mode and answer acknowledge defined in channel mode setup and channel answer setup.

## Diversity Limitations.

A diversity channel can only exist inside one system. It can not exist over 2 systems.

Max number of diversity channels in one system are 16

Max number of modules in a diversity channel are 32.

Do not mix modules from a normal diversity channel and MPT diversity channel!

If a command (except EXT MONITOR REQ) to diversity channel is referenced by one of its module numbers instead of the channel reference number the channel will stop running in diversity mode until the channel is in standby position by a disconnect or remove command.

## Co Channel Limitations.

A Co channel can only exist inside one system. It can not exist over 2 systems.

A Co channel must exist inside the same Com4500 rack unit and the subscriber modules must be HM808/2

Max number of Co channels in one system are 16

Max number of modules in a Co channel are 32.

Do not mix modules from a Co channel and MPT diversity channel

Co channel equipment is external to this application. We are just doing the keying and RX diversity selection.

All tone signalling will be on individual modules. No Co channel tone signalling !

If a command (except EXT MONITOR REQ) to Co channel is referenced by one of its module numbers instead of the Co channel reference number the channel will stop running in Co channel mode until the channel is in standby position by a disconnect or remove command. The only exception from this rule is HOOK command with tone signalling.

A Co channel can not be primary channel (owner) of any type of conference, but only participate as secondary channel of the conference.

## General Diversity & Co Channel Limitations.

The following commands are not supported:

- CONNECT REQ & EXT CONNECT REQ: CONN_REMOVEREF

## Set diversity setup

Set information about actual channel diversity setup

### SET DIVERSITY REQ.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Diversity Channel No. | Unsigned Short | 2 | 0 | 1 – 16 | Channel number |
| 4 | Channel setup | Char | 80 | Spaces |  | Comma separated text |
| 5 | Channel mode setup | Char | 80 | Spaces |  | Comma separated text |
| 6 | Channel answer setup | Char | 80 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Diversity channel number

Diversity channel number between 1 and 16. Define the channel for this setup frame

- Channel setup

Comma separated text defining the reference call number and the modules used for this diversity channel. (Reference No (512 to 64000), module 1, module 2, etc)

Channel setup=801,2,4,5,7

801 is the reference number used in Hook REQ, Connect REG, Ext connect REQ etc.

2,4,5,7 are the modules building the diversity channel.

CH1 to CH16 in P45453.ini diversity section.

P45453.ini

[Diversity]

;channel reference,modul1,modul2,modul3...,modul32

CH1=801,2,3,4,5

CH2=802,6,7,8,9

.

CH16=

- Channel mode setup

Comma separated text defining  mode information about the diversity channel. The string consist of 13 parameters. Mode1=02,30,03,20,20,1,1,1,0,1  ,0  ,0  ,0

Mode1=  to mode16=  in P45453.ini diversity section.

P45453.ini

[Diversity]

; 1: fast voting time x 110 ms

; 2: slow voting time x 110 ms (module busy)

; 3: tone RX voting time x 110 ms

; 4: time interval for updating  RSSI to master x 110 ms

; 5: wait time for tone acknowledge  x 110 ms

; 6: DIV. Co Channel

; 7: DIV. Tone TX Co Channel

; 8: DIV. Tone TX Pause

; 9: DIV. Squelch ACK

;10: DIV. Tone RX ACK

;11: DIV All Squelch Update

;12: DIV. All RSSI Update

;13: DIV. All Tone RX Update

;             1,  2,  3,  4,  5,  6,7,8,9,10,11,12,13

Mode1=02,30,03,20,20,1,0,1,0,1  ,0  ,0  ,0

;1- 02=Diversity in standby will shift to an other module if RSSI is better in 220 ms

;2- 30=Diversity in busy/connect will shift to an other module if RSSI is better in 3300 ms

;3- 03=Tone RX voting timeout is 330 ms. Timer reloaded for every RX acknowledge

;4- 20=Time interval for updating RSSI to master is 2200 ms. 0= no timer running

;5- 20=Wait time for tone acknowledge is 2200 ms

;6-  1=Diversity channel is running in Co Channel mode. 0=Normal diversity channel

;7-  1=Tone TX is using Co channel mode (not supported).

0= Tone TX using one module at a time

;8-  1=Tone TX is waiting for RX acknowledge between calls. 0= no pause between calls

;9- 1=Tone TX accept squelch as acknowledge. 0=do not accept squelch as acknowledge

;10-1=Tone TX accept Tone RX as acknowledge(Check answer setup)

;11-1=Diversity update squelch for every module. 0= update squelch for the channel

;12-1=Diversity update RSSI for every module. 0=update RSSI for the channel

:13-1=Diversity update tone RX for every module. 0=update tone RX for the channel.

;             1,  2,  3,   4,  5, 6,7,8,9,10,11,12,13

Mode2=02,30,03,20,20,1,0,1,0,1  ,0  ,0  ,0

.

Mode16=

- Channel answer setup

Comma separated text defining mobile answer to calls from Com4500

Answer1 to Answer16 in P45453.ini diversity section.

P45453.ini

[Diversity]

;Tone answer for diversity channel- Answer1 for channel 1, Answer2 for channel 2 etc

; Accept one of following RX answer from mobile when DIV. Tone RX ACK is used

; v indicates accept all digits

; The only limit in parameters are the total number of 80 char.

;       	1     ,2           ,3

Answer1=12vvv,vvvvvvv,35vvvB2vvvv

1=12vvv Accept 12000 to 12999 as tone RX acknowledge

2=vvvvvvv Accept 0000000 to 9999999 as tone RX acknowledge

2=35vvvB2vvvv Accept 35000B2000 to 35999B29999 as tone RX acknowledge

Answer2=17vvv,6vvvvvv,35vvvB5vvvv

..

Answer16=

Both channel reference and module number are stored in the SYS-INP command send from

Winser to App-server.

Examples:

MSG=SYS-INP;FCH=801;FMOD=1;TYPE=SQUELCH,1

MSG=SYS-INP;FCH=801;FMOD=1;TYPE=CALL;DIAL=CCIR,12345;RSSI=10

MSG=SYS-INP;FCH=801;FMOD=1;TYPE=SQUELCH,0

Either channel reference or module number may be used as TMOD identifier in the SYS-CON command send from App-server to Winser.

If TMOD holds the channel reference the module with the highest rssi-level will be selected.

If TMOD holds the module number the actual module number will be selected.

Examples:

MSG=SYS-CON;FMOD=10;TMOD=801;TYPE= CON-SINGLE

MSG=SYS-CON;FMOD=10;TMOD=1;TYPE= CON-SINGLE

### SET DIVERSITY Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Diversity Channel No. | Unsigned Short | 2 | 0 | 1 – 16 | Channel number |
| 4 | Chan setup | Char | 80 | Spaces |  | Comma separated text |
| 5 | Mode setup | Char | 80 | Spaces |  | Comma separated text |
| 6 | Answer setup | Char | 80 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Diversity channel number

Diversity channel number between 1 and 16.

- Channel setup

Comma separated text defining the reference call number and the modules used for this channel. (Actual channel setup in P45453.ini file)

- Mode setup

Comma separated text defining mode setup used for this channel

(Actual mode setup in P45453.ini file)

- Channel answer setup

Comma separated text defining mobile answer to calls from Com4500

(Actual answer setup in P45453.ini file)

## Get diversity setup

Get information about actual channel diversity setup on Com4500 server

### Get DIVERSITY REQ.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Diversity Channel No. | Unsigned Short | 2 | 0 | 1 – 16 | Channel number |

- ID.

Always zero

- MODE

Always zero.

- Diversity channel number

Diversity channel number between 1 and 16. Get setup info for this the channel

### GET DIVERSITY Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Diversity Channel No. | Unsigned Short | 2 | 0 | 1 – 16 | Channel number |
| 4 | Chan setup | Char | 80 | Spaces |  | Comma separated text |
| 5 | Mode setup | Char | 80 | Spaces |  | Comma separated text |
| 6 | Answer setup | Char | 80 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Diversity channel number

Diversity channel number between 1 and 16.

- Channel setup

Comma separated text defining the reference call number and the modules used for this channel. (Actual channel setup in P45453.ini file)

- Mode setup

Comma separated text defining mode setup used for this channel

(Actual mode setup in P45453.ini file)

- Channel answer setup

Comma separated text defining mobile answer to calls from Com4500

(Actual answer setup in P45453.ini file)

# Com52 input / output

Connecting a Com52 to a HM808/2 subscriber module make it possible to activate 6 output pins and receive input from 6 pins. Only some setup modes on HM808/2 support this facility.

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

## Com52 IO.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

MSG=COM52IO;TMOD=2;OUTPUT=001111 	output from master to server

MSG=COM52IO;TMOD=2;GETINTPUT=	 	Get input information from server

MSG=COM52IO;FMOD=2;INPUT=001111  	input from server to master

## Com52 IO Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Error Text | Char | 80 | Spaces |  | Text |
| 4 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

- Message

MSG=COM52IO;TMOD=2;OUTPUT=001111	response from server to master

MSG=COM52IO;FMOD=2;INPUT=001111  	response from / to server

## Output Command format:

MSG= COM52IO

TMOD=	;To HM808/2 subscriber module (1..n)

OUTPUT=	;6 pin ooutputs.  (000000..111111) – format. 0 =off. 1 = on

Transmit output to com4500 server module 2 from master control

MSG=COM52IO;TMOD=2;OUTPUT=001111

Response from server

MSG=COM52IO;TMOD=2;OUTPUT=001111 (OUTPUT is optional the others are mandatory)

## Get input Command format:

MSG= COM52IO

TMOD=	;To HM808/2 subscriber module (1..n)

GETINTPUT=	; Get input information

Get inputs from com4500 server module 2 to master control

MSG=COM52IO;TMOD=2;GETINPUT=

Response from server

MSG=COM52IO;FMOD=2;INPUT=000001

## Input Command format:

MSG= COM52IO

FMOD=	;From HM808/2 subscriber module (1..n)

INPUT=	;6 pin Input.  (000000..111111)  – format. 0 =off. 1 = on

Received inputs from com4500 server module 2

MSG=COM52IO;FMOD=2;INPUT=001111

Response from master control

MSG=COM52IO;FMOD=2;INPUT=001111 (INPUT is optional the others are mandatory)

# FAULTCMD

General information about card and connection fault

## Fault CMD.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

RACK=	Rack number 1 to 8

POS=	Position number 1 to 42

FAULT=	1 or 0	(1 = fault)

MSG=

POSTEXT, Fault text			(Card position fault)

- Message

RACK=	Rack number 1 to 8

CON= 	1 or 0	(1 = connect)

MSG=

RACKTEXT, Fault text			(Rack connection fault)

- Message

INTERCON=	1 or 0	(1 = connect)	(Server inter connection)

Card position 2 fault on rack 1

RACK=1;POS=2;FAULT=1;MSG=POSTEXT,HM815 [4]

[4] = start module number for card HM815

HM815 can use up to 30 subscriber (e.g. module 4 to 34)

Rack 1 connection fault

RACK=1;CON=0;MSG=RACKTEXT, Rack 1 disconnected

RACK=1;CON=1;MSG=RACKTEXT, Rack 1 connected

Interconnect fault

INTERCON=1		Inter connection between servers	(Winser32.exe)

INTERCON=0		No inter connection between servers 	(Winser32.exe)

# TE1040/TE1039/CB4200 CMD

A TE10-40, a CB4200 box a TE10-39/3 or connected to HM807/2 or HM807/3 or Hm817 can only receive or transmit commands after Com4500 has received a CONNECT or CB_CONNECT from the box.

When a CONNECT or CB-CONNECT is received the master control application have to set up all parameters for the box.

## TE1040, TE1039 and CB4200  CMD.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

MSG=COMMAND, parameter 1, parameter 2 ….. parameter n

## TE10-40 and TE10-39/3 Box command

### CONNECT from Com4500 to master application

Both TE10-40 and TE10-39/3

Before a TE10-40 box or a TE10-39/3 box can receive any command you have to receive a connect command from the box, indicating the HM807/2 or HM817 module communicate with the box.

MSG=CONNECT

FMOD=	From Module / box number

CON=		1 or 0  (1 = connect)

RACK=	1 to 8  (i.e. Module in rack 1)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=CONNECT;FMOD=12;CON=0;RACK=1	(Box 12 rack 1 disconnected)

MSG=CONNECT;FMOD=12;CON=1;RACK=1 	(Box 12 rack1  connected)

### Matrix command from master application to Com4500

Both TE10-40 and TE10-39/3

A matrix command can connect one or more inputs to an output with level facility

From master control to Com4500

MSG=MATRIX

TMOD=	Module / Box number receiving the command

HEAD1= 	Muting 0 to 63 dB. Values greater than 63 equal off (Headset 1)

HEAD2=	Muting 0 to 63 dB. Values greater than 63 equal off (Headset 2)

ISDNA=	Muting 0 to 63 dB. Values greater than 63 equal off (ISDN A/NET A)

ISDNB=	Muting 0 to 63 dB. Values greater than 63 equal off (ISDN B/NET B)

SOUND=	Muting 0 to 63 dB. Values greater than 63 equal off

(SoundBlaster)

AUX1=	Muting 0 to 63 dB. Values greater than 63 equal off (Auxiliary 1)

AUX2=	Muting 0 to 63 dB. Values greater than 63 equal off (Auxiliary 2)

TE10-40 only:

PHONE=	Muting 0 to 63 dB. Values greater than 63 equal off (Phone)

TE10-39/3 and TE10-40/3 only:

MIC=	Muting 0 to 63 dB. Values greater than 63 equal off (Micr-ph).

TE10-40 only:

OUT= 	HEADR or HEADL or LSR or LSL

HEADR	Headset Right

HEADL	Headset Left

LSR		Loudspeaker Right

LSL		Loudspeaker Left

TE10-39/3 only:

OUT= 	HEADR or HEAD1L or HEAD2L or LSR or LSL

HEADR	Headset Right (both headset 1 and 2)

HEAD1L	Headset 1 Left

HEAD2L	Headset 2 Left

LSR		LoudSpeaker Right / Internal LoudSpeaker

LSL		LoudSpeaker Left

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

Matrix command connecting ISDNB muting 0 dB and SoundBlaster muting 6 dB to Headset Right output use module 2

MSG=MATRIX;OUT=HEADR;ISDNB=0;SOUND=6;TMOD=2

Matrix command connecting Headset 1 muting 10 dB and SoundBlaster muting 6 dB to Headset Left output use module 2

MSG=MATRIX;OUT=HEADL;HEAD1=10;SOUND=6;TMOD=2

### AGC command from master application to Com4500

TE10-40 only

An AGC command can enable or disable AGC control

From master control to Com4500

MSG=AGC

TMOD=	Module / Box number receiving the command

HEAD1=	0,0 (input, output) 	0 = off	1 = on	(Headset 1)

HEAD2=	0,0 (input, output) 	0 = off	1 = on	(Headset 2)

ISDNA=	0,0 (input, output) 	0 = off	1 = on	(ISDN A)

ISDNB=	0,0 (input, output) 	0 = off	1 = on	(ISDN B)

SOUND=	0,0 (input, output) 	0 = off	1 = on	(SoundBlaster)

PHONE=	0,0 (input, output) 	0 = off	1 = on	(Phone)

AUX1=	0,0 (input, output) 	0 = off	1 = on	(Auxiliary 1)

AUX2=	0,0 (input, output) 	0 = off	1 = on	(Auxiliary 2)

LSR=	0 = output off	1 = output on		(Loudspeaker Right)

LSL=	0 = output off	1 = output on		(Loudspeaker Left)

TE10-40/3 only:

MIC=		0,0 (input, output) 	0 = off	1 = on	(External Mic)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=AGC;TMOD=2;AUX2=1,0;ISDNB=0,0

### FLASHSETUP command from master application to Com4500

TE10-40 only

The FLASHSETUP command controls the flash setup of the box unit.

MSG=FLASHSETUP

TMOD=	Module / Box number receiving the command

MODE=	0 = Clear all settings

1 = Load default setup

2 = Save default setup

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=FLASHSETUP;TMOD=2;MODE=0

### Output command from master application to Com4500

Both TE10-40 and TE10-39/3

An output command can activate LED or relay outputs

From master control to Com4500

MSG=OUTPUT

TMOD=	Module / Box number receiving the command

AUX1=	10,10,255 	(Pulse * 10ms, pause *10ms, repeat = number of

times 255= forever)

AUX2=	10,10,255 	(Pulse * 10ms, pause *10ms, repeat = number of

times 255= forever)

TE10-40 Only:

LEDA=	10,10,255 	(Pulse * 10ms, pause *10ms, repeat = number of

times 255= forever)

LEDB=	10,10,255 	(Pulse * 10ms, pause *10ms, repeat = number of

times 255= forever)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=OUTPUT;TMOD=2;AUX2=10,10,255

### Input command from Com4500 to master application

Both TE10-40 and TE10-39/3

An input command detects headset key or other inputs

From Com4500 to master control

MSG=INPUT

FMOD=		Command from Module / Box number

HEAD1KEY=		0= off	1 = on	(Handset 1 key)

HEAD2KEY=		0= off	1 = on (Handset 2 key)

HEAD1CON=	0= off	1 = on (Handset 1 disconnected/connected)

HEAD2CON=	0= off	1 = on (Handset 2 disconnected/connected)

EXTKEY=		0= off	1 = on (External key)

AUX1=		0= off	1 = on	(Auxiliary 1)

AUX2=		0= off	1 = on	(Auxiliary 2)

Command are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=INPUT;FMOD=2;AUX2=1

### Level command from master application to Com4500

Both TE10-40 and TE10-39/3

General volume control for a TE10-40 box or TE10-39/3 box.

From master control to Com4500

MSG=LEVEL

TMOD=	Module number receiving the command

HEAD1=  	0,0 (input: +14dB -> -16dB, output: +6dB -> -36dB)	(Headset 1)

HEAD2=	0,0 (input: +14dB -> -16dB, output: +6dB -> -36dB)	(Headset 2)

SOUND=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)   (SoundBlaster)

AUX1=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)	(Auxiliary 1)

AUX2=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)	(Auxiliary 2)

LSR=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)  (Loudspeaker Right)

LSL=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)  (Loudspeaker Left)

TE10-40 only:

PHONE=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)	(Phone)

TE10-39/3 only:

HEADR=	0,0 (input: +14dB -> -16dB, output: +6dB -> -36dB)  (Headset 1-2/Right)

TE10-39/3 and TE10-40/3 only:

MIC=	0,0 (input: +20dB -> -10dB, output: +6dB -> -36dB)	(Mic)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=LEVEL;TMOD=2;HEAD1=3,-6

## TE10-39/3 Box command

### Display command from master application to Com4500

Operates display on TE10-39/3 unit.

MSG=DISPLAY

TMOD=	Module number receiving the command

WIN=w	       	w = window 0 to 4    (optional. Default window = 0)

MODE=ab		a: 0 = no action. 1 = set window active after writing.

b: 0 = no action. 1 = clear window before writing.

Tn=X,Y,F(abcd),’User Text’

n: number to distinguish texts.

X: 1-16 horizontal position

Y: 1-8 vertical position

F (optional): Format specifier.

a: 0 = no action, 1= Invert text

b: 0 = no action, 1= Underline text

c: 0 = no action, 1= Overline text

d: 0 = no action, 1= Flash text

T1= X,Y,’HELLO WORLD1’,

1.text:        X = 1-16 horizontal position, Y = 1-8 vertical position,

T2= X,Y,F,’HELLO WORLD2’,

2.text         F (format specifier):

T3= X,Y,’HELLO WORLD3’,    3.text

T4= X,Y,’HELLO WORLD4’,    4.text

…

T10= X,Y,’HELLO WORLD n’,   10.text:  (within max length of command string[255])

CHAR0=abcdefgh	8 bytes to describe a char pattern. Overwrites existing char.

…

CHAR255=abcdefgh

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

Set active window:

MSG= DISPLAY;TMOD=1;WIN=0;MODE=1

Clear window:

MSG= DISPLAY;TMOD=1;WIN=0;MODE=11

Write texts, T4 is inverted and flashes:

MSG=DISPLAY;TMOD=1;WIN=0;MODE=1;T1=1,1,’HELLO WORLD1’; T2=1,2,’HELLO WORLD2’;T3=1,3,’HELLO WORLD3’;T4=1,4,1001,’HELLO WORLD4’

Define custom character patterns:

MSG=DISPLAY;TMOD=1;CHAR1=007e444850607e00

### Key command from Com4500 to master application

Key input from TE10-39/3 keyboard. Keys are organized as follows.

|  | Function keys |  | Numeric keys |  |
| --- | --- | --- | --- | --- |
|  | A (0x10) | B (0x11) | C (0x12) | D (0x13) | E (0x14) |  | S (0x1F) | 1 (0x01) | 2 (0x02) | 3 (0x03) |  |
|  |  |  |  |  |  |  | < (0x0B) | 4 (0x04) | 5 (0x05) | 6 (0x06) |  |
|  | F (0x15) | G (0x16) | H (0x17) | I (0x18) | J (0x19) |  | > (0x0A) | 7 (0x07) | 8 (0x08) | 9 (0x09) |  |
|  | K (0x1A) | L (0x1B) | M (0x1C) | N (0x1D) | O (0x1E) |  | C (0x0C) | * (0x0E) | 0 (0x00) | # (0x0F) |  |

Headset Volume Slider	0x50

HT Volume Slider		0x51

MSG=KEY

FMOD=	From Module / box number

KEY=ab,vol

a:      KEY number

b:      R: release, C: slider change (Volume sliders ony)

vol:   0-255 volume value (0=min, 255=max). (Volume sliders ony).

Key 5 on:

MSG=KEY, TMOD=1, KEY=5

Key 10 off:

MSG=KEY;TMOD=1;KEY=10R

HT Volume slider changed:

MSG=KEY;TMOD=1;KEY=50C,126

### Led command from master application to Com4500

Controlling LEDs on keyboard. LEDs are organized as follows.

|  | Function keys |  | Numeric keys |  |
| --- | --- | --- | --- | --- |
|  | L1 | L2 | L3 | L4 | L5 |  | L16 |  |  |  |  |
|  | L6 | L7 | L8 | L9 | L10 |  |  |  |  |  |  |
|  | L11 | L12 | L13 | L14 | L15 |  |  |  |  |  |  |

MSG=LEDS

TMOD=	          Module number receiving the command

L0=a		     make L1- L16 = L0

L1=a	       	     L1- L16: Led 1 to 16

L2=a		     a:  red led

..		     0 = off

..		     1 = on

..		     2 = flash1	(timings, see MSG SETUP)

L16=a		     3 = flash2	(timings, see MSG SETUP)

Led 1: on

MSG=LEDS;TMOD=1;L1=1

Led 1: off;  Led 2: on; Led 3: flash2

MSG=LEDS;TMOD=1;L1=0;L2=1;L3=3

All leds off;  Led 3: on

MSG=LEDS;TMOD=1;L0=0;L3=1

### Attention command from master application to Com4500

Controlling Attentiontones in box.

MSG=ATTENTION

TMOD=	          Module number receiving the command

ATT=a,b,c,d,e	,f

a = 1.tone frequency (128-4000Hz), <128 = notone/silence

b = 1.tone duration x 0,01s, 0 = continuously

c = 2.tone frequency (128-4000Hz), <128 = notone/silence

d = 2.tone duration x 0,01s, 0 = no 2.tone (skip tone)

e = repeat tones a number of times 1-254, 0 = never repeat, 255 = infinite

f = repeat attentiontone (a-e) after a number of seconds 1-15, 0 = never repeat

ATT=a

a:  pre coded tone 1-4

Continuous tone: 425Hz:

MSG=ATTENTION;TMOD=1;ATT=425,0,0,0,0,0

Switched tone: 5 x 625/950Hz, 70 ms repeated each 5 sec:

MSG=ATTENTION;TMOD=1;ATT =625,7,950,7,10,5

Precoded tone 1:

MSG=ATTENTION;TMOD=1;ATT=1

### Setup from master application to Com4500

MSG= SETUP

TMOD=Module number receiving the command

SETUP=a,b,c,d,e

a:  display backlight:             range 0-255   default 3    (0 = max, 255 = min)

b:  display backlight color    range 0-7       default 7    (bit0=red,bit1=green,bit2=blue)

c:  display contrast:               range 0-255  default 160 (0 = min, 255 = max)

d:  key delay x 0,01 sec.	range 1-255   default 6 = 0,060 sec.   (0 = ignore)

e:  attention tone volume:      range 0-15     default 8    (0 = min, 15 = max)

LED1=a,b	Pre coded led flash pattern 1 (flash1).

a = on time x 0,01s, default 50

b = off time x 0,01s, default 50

LED2=a,b	Pre coded led flash pattern 2 (flash2) .

a = on time x 0,01s, default 50

b = off time x 0,01s, default 50

ATT1= a,b,c,d,e,f

Pre coded attention tone 1.  syntax = ATTENTION  (default off)

ATT2=a,b,c,d,e,f

Pre coded attention tone 2.  syntax = ATTENTION  (default off)

ATT3=a,b,c,d,e,f

Pre coded attention tone 3.  syntax = ATTENTION  (default off)

ATT4=a,b,c,d,e,f

Pre coded attention tone 4.  syntax = ATTENTION  (default off)

RESET=abc

a:  1 = clear active window

b:  1 = clear all windows

c:  1 = all leds off

d:  1 = stop any attentiontones

ignore:  any character <>  1

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

General Setup with 2 pre coded flash patterns.

MSG=SETUP;TMOD=1;SETUP=50,3,75,10;LED1,10,10; LED2=10,100

Changing display while running:

MSG=SETUP;TMOD=1;SETUP=20,4,40

Stop leds and clear all windows:

MSG=SETUP;TMOD=1;RESET=011

## CB4200 Box command

### CB-CONNECT from Com4500 to master application

Before a CB4200 box can receive any command you have to receive a connect command from the box, indicating the HM807/2 module communicate with the box.

MSG=CB-CONNECT

FMOD=	From Module / box number

CON=		1 or 0  (1 = connect)

RACK=	1 to 8  (i.e. Module in rack 1)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=CB-CONNECT;FMOD=12;CON=0;RACK=1 (Box 12 rack 1 disconnected)

MSG=CB-CONNECT;FMOD=12;CON=1;RACK=1 (Box 12 rack1  connected)

### CB-Display:	   Display control

MSG=CB-DISPLAY

WIN=w	       	w = window 0 to 7    (optional. Default window = 0)

MODE=abc		a: 0 = no action. 1 = set window active after writing.

b: 0 = no action. 1 = clear window before writing.

c: 0 = no action, 1 = scroll up, 2 = scroll down

CUR=X,Y,F		cursor on:  	X = 1-16 horizontal position,

Y = 1-4 vertical position

cursor off: X = 0

F (optional) : 1 = 1-line cursor,  2 = 1/8 line blinking cursor

no action:  CUR command missing

RECT=X1,Y1,X2,Y2,F

Window top-left:         	X1 = 1-16 horizontal position,

Y1 = 1-4 vertical position

Window bottom-right: 	X2 = 1-16 horizontal position,

Y2 = 1-4 vertical position

F (optional): 0 = normal text, 1 = reverse text,  2 = blink text

T0= X,Y,F, ’HELLO WORLD’

Scroll line: X = 0, Y = 0, F: 0 = normal text, 1 = reverse text,  2 = blink text

T1= X,Y,F,’HELLO WORLD1’,

1.text:        X = 1-16 horizontal position, Y = 1-4 vertical position,

T2= X,Y,F,’HELLO WORLD2’,

2.text         F (optional): 0 = normal text, 1 = reverse text,  2 = blink text

T3= X,Y,F,’HELLO WORLD3’,    3.text

T4= X,Y,F,’HELLO WORLD4’,    4.text

…

T10= X,Y,F,’HELLO WORLD n’,   10.text:  (within max length of command string[255])

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

Set active window:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=1

Clear window:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=11

Clear partial window:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=11;RECT=1,1,8,4

Cursor on:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=1;CUR=8,2

Cursor off:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=1;CUR=0

Scroll up:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=101;RECT=1,1,8,4;

T0=0,0,1,’TOP LINE’

Scroll down:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=102;RECT=1,1,8,4; T0=0,0,1,’BOTTOM LINE’

Menu without scrolling:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=1;RECT=1,1,8,4;T0=0,2,1

Write texts:

MSG=CB-DISPLAY;TMOD=1;WIN=0;MODE=1;T1=1,1,’HELLO WORLD1’; T2=1,2,’HELLO WORLD2’;T3=1,3,’HELLO WORLD3’;T4=1,4,1,’HELLO WORLD4’

### CB-Led:		   Led control

MSG=CB-LEDS

L0=ab		     make L1- L44 = L0

L1=ab	       	     L1- L44: Led 1 to 44

L2=ab		     a:  top led (red)   b:  bottom led (green).

..		     0 = off

..		     1 = on

..		     2 = flash1	(on: 0,50 sec, off: 0,50 sec)

..		     3 = flutter	(on: 0,06 sec, off: 0,02 sec)

..		     4 = wink	(on: 0,95 sec, off: 0,05 sec)

..		     5 = flash2	(on: 0,12 sec, off: 0,12 sec)

L44=ab	     6 = flash3	(on: 1,00 sec, off: 1,00 sec)

Led 1: a = on, b = flash1

MSG=CB-LEDS;TMOD=1;L1=12

Led 1: a = off, b = on;  Led 2: a = on, b = off;  Led 3: a = on, b = on

MSG=CB-LEDS;TMOD=1;L1=01;L2=10;L3=11

All leds off;  Led 3: a = on, b = on

MSG=CB-LEDS;TMOD=1;L0=00;L3=11

### CB-Attention:	   Attention tone

MSG=CB-ATTENTION

ATT=a,b,c,d,e

a = 1.tone, b = 2.tone, c = timing, d = number of tones, e = repeat time

a and b:	0 = notone

1 = 425 Hz

2 = 500 Hz

3 = 625 Hz

4 = 700 Hz

5 = 781 Hz

6 = 950 Hz

7 = 977 Hz

8 = 1100 Hz

9 = 1250 Hz

10 = 1400 Hz

11 = 1550 Hz

12 = 1700 Hz

13 = 1800 Hz

14 = 2000 Hz

15 = 1900 Hz

c:  time each tone x 10 ms   range: 0-255     (0 = infinitive)

d:  number of tones,             range: 0-15       (0 = infinitive)

e:  repeat time x 1 sec,         range: 0-15       (0 = repeat off)

ATT=a	                                a:  pre coded tone 1-4

Continuous tone: 425Hz:

MSG=CB-ATTENTION;TMOD=1;ATT=1,0,0,0,0

Single tone: 1 x 625 Hz, 500 ms:

MSG=CB-ATTENTION;TMOD=1;ATT =3,0,50,1,0

Switched tone: 5 x 625/950Hz, 70 ms repeated each 5 sec:

MSG=CB-ATTENTION;TMOD=1;ATT =3,6,7,10,5

### CB-SETUP:	   Setup

MSG=CB-SETUP

SETUP=a,b,c,d,e,f,g,h

a:  display backlight:             range 0-10     default 7    (0 = 0%, 10 = 100%)

b:  display contrast:               range 0-15     default 15   (0 = min, 15 = max)

c:  attention tone volume:      range 0-15     default 8    (0 = min, 15 = max)

d:  speaker monitor volume:  range 0-15     default 8    (0 = min, 15 = max)

e:  key delay x 0,1 sec.	range 1-15     default 10 = 1,0 sec.   (0 = ignore)

f:  key repeat rate x 0,1 sec.	range 1-15     default 3 = 0,3 sec.   (0 = ignore)

g:  cursor type: 	0 = ignore

1 = 1-line cursor

2 = 1/8-line blinking cursor  (default)

h:  0 = ignore. 1 = enable key klick for all keys

ATT1=a,b,c,d,e

Pre coded attention tone 1.  syntax = CB-ATTENTION  (default off)

ATT2=a,b,c,d,e

Pre coded attention tone 2.  syntax = CB-ATTENTION  (default off)

ATT3=a,b,c,d,e

Pre coded attention tone 3.  syntax = CB-ATTENTION  (default off)

ATT4=a,b,c,d,e

Pre coded attention tone 4.  syntax = CB-ATTENTION  (default off)

K1=abc     K1-K44:  Keyboard keys 1 to 44

K2=abc

a:  0 = action on key press (default), 1 = action on both key press and key release

b:  0 = key click off (default), 1 = key click on

c:  0 = repeat off (default), 1 = repeat on

..

K44=abc

RESET=abcdefgh

a:  1 = clear active window

b:  1 = all leds off

c:  1 = stop any attention

d:  x = not used

e:  1 = all audio connections off

f:   x = not used

g:  x = not used

h:  1 = clear all windows

ignore:  any character <>  1

AF=abcdefgh

a:  0 = mic.(s) off.              1 = mic(s) on

b:  0 = off	                     1= B-channel to ext speaker

c:  0 = speaker ext off.      1 = speaker ext on

d:  0 = speaker int off.       1 = speaker int on

e:  0 = earpiece(s) off.       1 = earpiece(s) on

f:   0 = off.                         1 = split A and B-channel

g:  0 = listen control min.  1 = listen control max

h:  0 = voice control off.    1 = voice control on

ignore:  any character <> 0 and 1

General Setup with 2 pre coded tones, one ptt-button (K1) and one button (K2) with repeat facility:

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=CB-SETUP;TMOD=1;SETUP=7,15,8,8,10,3,2,1;ATT1=3,0,50,1,0; ATT2=7,0,10,1,0;K1=100;K2=011

Changing display and volume while running:

MSG=CB-SETUP;TMOD=1;SETUP=7,15,8,8

Switching mic on, ext speaker off, int speaker on and earpiece on:

MSG=CB-SETUP;TMOD=1;AF=1x011xxx

Stop any attention tone and clear all windows:

MSG=CB-SETUP;TMOD=1;RESET=00100001

### CB-Key:		   Input from keyboard

MSG=CB-KEY

KEY=ab

a: 1-44:  keyboard keys 1-44

59:  headset on/off

60:  hook on/off

61:  ext key on/off

62:  handset key on/off

63:  headset key on/off

b:      R: release

Key 5 on:

MSG=CB-KEY, TMOD=1, KEY=5

Handset key on:

MSG=CB-KEY;TMOD=1;KEY=62

Handset key off:

MSG=CB-KEY;TMOD=1;KEY=62R

## TE1040 CMD Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Error Text | Char | 80 | Spaces |  | Text |
| 4 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

- Message

MSG=Command string from TE1040CMD

# MPT1343  Command format.

Command: SYSCMD=350 and SYSCMD structure

Response:  SYSCMD+1  and SYSCMD response structure

The system is not supporting the 1343 specification. Making a few calls from a standard 1343 radio to our local system is the intention. The success is depending of the facilities of the radio such as timeslot and diversity setup.

A MPT system consist of one or more control channels and one or more traffic channels.

The system can consist of individual control and traffic channels or control and traffic channels running in locked site diversity mode.

The number calling sequence for MPT is: Fleet-number+Unit-number;

A number-prefix (NP 200 to 327) is separately defined for every control channel

Maximum number of units in one fleet are 700 for a 3 digit system and 70 for a 2 digits system.

Maximum number of group units in one fleet are 100 for a 3 digit system and 10 for a 2 digits system. Maximum individual numbers using the same prefix are 8100.

## Control channel Limitations.

A MPT Control channel can only exist inside one system. It can not exist over 2 systems.

Max number of control channels in one system are 4

Max number of sites for a control channel are 16.

Defining 2 or more sites on one control channel will course the channel/system to run in locked site diversity mode. The site of the control channel site with best RSSI, will select one of the traffic channels on that site for conversation. The traffic channel / site used will not change during conversation (not running in diversity mode)

Co channel mode is not supported. Do not mix modules from a MPT diversity channel and  modules from a Co channel or normal diversity channel

Timeslot can be defined 1 to 3 times 110 ms (only timeslot 2 and 3 are supported)

## Traffic channel Limitations.

A MPT  traffic channel can only exist inside one system. It can not exist over 2 systems.

The traffic channels must exist in the same system as its corresponding control channels.

Max number of traffic channels in one system are 8

Max number of sites for a traffic channel are 16.

Defining 2 or more sites on one traffic channel will not course the channel to run in diversity mode. Only the control channel will use diversity mode.

Co channel mode is not supported. Do not mix modules from a MPT diversity channel and  modules from a Co channel or normal diversity channel

## Command Limitations.

The MPT support for the moment only normal SPEECH and Extension Speech call to and from modules, Emergency and extension Emergency call from modules, Go To Channel, Status calls, DATA short messages (22 char 8 bit, 25 char 7 bit) ,CANCEL, PRESSEL, CLEAR call for shutting a conversation down and different types of ACK for acknowledge.

No support for all other MPT calls including:

NPD data calls.

## MSG command Application Server(master) -> Com4500-TSC:

MSG=MPT-OUT

TYPE=

CALL:		Call

GTC:		Got to channel call or GTC,xxxx for xxxx=8101 or 8102

STATUS, x:	Status call

DATA:		Short data call (22 char 8 bit or 25 char 7 bit)

CLEAR:	Clear-down command from radio

NACK:		System Acknowledge rejection

SETSETUP:	Set MPT1343 information on server

GETSETUP:	Get MPT1343 information From server

ACK:		Acknowledge

ACK2:		Two times Acknowledge

ACKB:		Call queued Acknowledge

ACKI:		Wait Acknowledge

ACK,8185:	Registration Acknowledge

ACKV:		Subscriber absent Acknowledge

ACKX:		Rejection invalid Call

ACKX,8185:	Rejection - Registration Acknowledge

All types of acknowledge except ACK2 can have the extension ,xxxx  i.e. ACKB,xxxx for xxxx= 1 to 4 digits

## MSG command Com4500-TSC -> Application Server (master):

MSG=MPT-INP

TYPE=

REG,8185:	 	Registration

CALL:		 	Speech call

CALL, xxxx:	 	Extension Speech call with TFIN=0 and TUN=0 and

xxxx= 1 to 4 digits

EMERG:	 	Emergency call using FUN and TUN

EMERG, xxxx:		Extension Emergency call with TFIN=0 and TUN=0 and

xxxx= 1 to 4 digits

CON:		 	Connection on traffic channel / traffic module

PRESSEL, x:	 	PRESSEL on traffic channel / traffic module x=1 or 0

STATUS, xx:	 	Status call for xx= 1 to 31

DATA:		 	Short data call  (22 char 8 bit or 25 char 7 bit)

CLEAR:	 	Speech call clear-down to radio

CANCEL:	        	Call cancellation

CANCEL, x:        	Extension cancellation

SETUP:		Setup information on COM4500

NACK:			System Acknowledge rejection

ACK:		 	Acknowledge

ACK, x:	 	Acknowledge with rejection

ERR			Error text

## Default setup before using MPT1343

Before the MPT1343 command set can be used you have to define a at least on control channel and its default setup parameters in P45453.ini. You can use an editor or SETSETUP command.

CH1=801,2,1   (channel reference number, radio frequency channel, internal module number)

DEF1=FFIN=2001;FUN=201;  (2001 – to and from Fleet number, 201 calling unit)

MODE1=201,2,2,2,3 (NP=201, Time slot=2, Pause slot=2, Voting slot=2, LET time=3)

FLLET1=2,700,2001,200 (Min individual number, Fleet Size, Fleet number, Fleet Offset)

Status call to mobile unit 301 on control channel 1 from master control using default preloaded setup:  MSG=MPT-OUT; TYPE=STATUS,3;TUN=301;CCH=801

## Command syntax

KEYWORD=parameter, parameter, parameter; (Keyword separator)

TYPE=DATA, ”Hello world” (parameter surrounded by double quotes (“))

KEYWORD1=parameter; KEYWORD2=parameter; KEYWORD3=parameter

MSG=MPT-OUT;TYPE=CALL;TUN=201

MSG=MPT-OUT;TYPE=DATA, ”Hello world”; TUN=201

## Command format:

Optional commands can be defined and loaded from the P45453.ini file.

MSGNO=	; Session number identifying the call (0-FFFF hex)	(optional)

FFIN=		;From Fleet individual number				(optional)

FUN=		;From Unit number (normally loaded by master)		(optional )

TFIN=		;To Fleet individual number				(optional )

TUN=		;To Unit number (normally loaded by master) 		(mandatory)

CCH=		;Control channel				(mandatory)

CMOD=	;Used Control channel module. Information from server to master

TCH=		;Traffic channel					(optional used by speech call)

TMOD=	;Used Traffic channel module. Information from server to master

FMOD=	;From module number by speech call		(mandatory  by speech call)

DIAL=		;Digits to a subscriber - for example PABX

TYPE=								(mandatory)

REG,8185

CALL, x

EMERG, x

GTC

CON

PRESSEL, x	(x= 1 or 0)

STATUS, xx 	(range 1 to 31)

DATA, HELLO WORLD

CLEAR

GETSETUP,

SETSETUP,

NACK

ACK

ACK2

ACKB

ACKI

ACKV

ACKX

Complete specified status call to mobile unit on control channel 1 from master control

MSGNO if used is incremented for every command transmitted from master to Com4500

MSG=MPT-OUT;TYPE= STATUS,03; TNP=201; TFIN=2001;TUN=301; FNP=201; FFIN=2001;FUN=201;CCH=801

Using CALL without FMOD loaded will just check the reach ability for the MPT unit (301).

MSG=MPT-OUT;TYPE= CALL;FUN=301;CCH=801

## Command from Application Server (master)

Command examples with only one fleet in the system and using the default setup

FFIN=2001 and TFIN=2001

CH1=801,1,16			Control channel 1 using module 16

TR1=901,2,17			Traffic channel 1 using module 17

MODE1=201,2,2,2,3		Mode setup for control channel 1 using NP=201

### CALL

Speech call to mobile unit 301 from unit 201 on control channel 1 connecting to module 2:  MSG=MPT-OUT; TYPE=CALL;TUN=301;FUN=201;CCH=801;TCH=901;FMOD=2

Acknowledge

MSG=MPT-INP; TYPE=ACK; TFIN=2001; TUN=201; FFIN=2001; FUN=301; CCH=801; CMOD=16

GTC

The system automatically generate a local GTC (go to channel) to unit 301

Connection

MSG=MPT-OUT; TYPE=CTC; TFIN=2001; TUN=201; FFIN=2001; FUN=301; CCH=801; CMOD=16;

MSG=MPT-INP; TYPE=CON; TCH=901; TMOD=17;FMOD=2

### STATUS, x

Status 3 call to mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-INP; TYPE= STATUS,03; TUN=301; FUN=201; CCH=801

Acknowledge

MSG=MPT-INP; TYPE=ACK; TFIN=2001; TUN=201; FFIN=2001; FUN=301; CCH=801; CMOD=16

### DATA, text

Text call to mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-OUT; TYPE= DATA,“Hello world”;  TUN=301; FUN=201; CCH=801

Acknowledge

MSG=MPT-INP; TYPE=ACK;  TFIN=2001; TUN=201; FFIN=2001; FUN=301; CCH=801; CMOD=16

### CLEAR

Clear call to mobile unit 301 from unit 201 on traffic channel 1 using module 17:

MSG=MPT-OUT; TYPE=CLEAR; TUN=301; FUN=201; CCH=801; TMOD=17; FMOD=2

### GTC

Mobile unit 301 go to traffic channel 1 from unit2 on control channel 1:

MSG=MPT-OUT; TYPE=GTC; TUN=301; FUN=201; CCH=801; TCH=901

Only accepted MPTCMD Response is received on this command

ACK, x if not accepted

### ACK,8185

Registration acknowledge to mobile unit 301 on control channel 1:

MSG=MPT-OUT; TYPE=ACK,8185; TFIN=2001;TUN=301; CCH=801; CMOD=16

### ACK

General Acknowledge to mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-OUT; TYPE=ACK; TFIN=2001; TUN=301; FFIN=2001; FUN=201; CCH=801; CMOD=16

### ACK2

Acknowledge two times to mobile unit 301 from unit 201 on control channel 1: (On DATA call)

MSG=MPT-OUT; TYPE=ACK2; TFIN=2001; TUN=301; FFIN=2001;FUN=201;CCH=801; CMOD=16

### ACKB

Acknowledge Call queued to mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-OUT; TYPE=ACKB; TFIN=2001;TUN=301;FFIN=2001;FUN=201;CCH=801; CMOD=16

### ACKI

Acknowledge wait to mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-OUT; TYPE=ACKI; TFIN=2001;TUN=301;FFIN=2001;FUN=201;CCH=801; CMOD=16

### ACKV

Subscriber absent Acknowledge mobile unit 301 from unit 201 on control channel 1:

MSG=MPT-OUT; TYPE=ACKV; TFIN=2001;TUN=301;FFIN=2001;FUN=201;CCH=801; CMOD=16

### ACKX

Rejection invalid Acknowledge Call to mobile unit 301 from unit 201 on control channel 1:  MSG=MPT-OUT; TYPE=ACKX; TFIN=2001;TUN=301;FFIN=2001;FUN=201;CCH=801; CMOD=16

### ACKX,8185

Registration Rejection acknowledge to mobile unit 301 on control channel 1:

MSG=MPT-OUT; TYPE= ACK,8185; TFIN=2001;TUN=301;CCH=801; CMOD=16

## Command from Com4500-TSC

No MSGNO=xx is used in commands from Com4500

Command examples with only one fleet in the system and using the default setup

FFIN=2001 and TFIN=2001

CH1=801,1,16			Control channel 1 using module 16

TR1=901,2,17			Traffic channel 1 using module 17

MODE1=201,2,2,2,3		Mode setup for control channel 1 using NP=201

FLEET1=2,700,2001,200	Fleet setup

### REG,8185

Registration(8185) from unit 301 on control channel 1

MSG=MPT-INP; TYPE= REG,8185; FFIN=2001;FUN=301;CCH=801;CMOD=16

Acknowledge

MSG=MPT-OUT; TYPE= ACK,8185; TFIN=2001; TUN=301; CCH=801; CMOD=16

Rejection Acknowledge

MSG=MPT-OUT; TYPE= ACKX,8185; TFIN=2001; TUN=301; CCH=801; CMOD=16

### CALL

Speech call to unit 201 from mobile unit 301on control channel 1:

MSG=MPT-INP; TYPE= CALL; TFIN=2001;TUN=201; TFIN=2001; FUN=301; CCH=801

Acknowledge

MSG=MPT-INP; TYPE= ACKB; TFIN=2001; TUN=301; FFIN=2001; FUN=201;CCH=801; CMOD=16

### CALL, x

X: extension qualifier depends on the master application.

Extension Speech call to 9000 from mobile unit 301on control channel 1:

MSG=MPT-INP; TYPE= CALL,9000; TFIN=2001;FUN=301;CCH=801; CMOD=16

Acknowledge

MSG=MPT-OUT; TYPE= ACKB,9000; TFIN=2001;TUN=301;CCH=801; CMOD=16

Extension Speech call (i.e. PABX) to 123456789 from mobile unit 301on control channel 1:

MSG=MPT-INP; TYPE= CALL,xxxx; TFIN=2001;FUN=301;CCH=801; CMOD=16; DIAL=123456789

Acknowledge

MSG=MPT-OUT; TYPE= ACKB,xxxx; TFIN=2001;TUN=301;CCH=801; CMOD=16

Xxxx= 8101 PSTN or 8102 PABX

Go to channel and make connection to module 2

MSG=MPT-OUT; TYPE= GTC,xxxx; TFIN=2001;TUN=301;CCH=801; CMOD=16;TCH=901;FMOD=2

### EMERGENCY

Emergency call to unit 201 from mobile unit 301 on control channel 1:

MSG=MPT-INP; TYPE= ENERG; TFIN=2001; TUN=201; TFIN=2001; FUN=301; CCH=801; CMOD=16

Acknowledge

MSG=MPT-OUT; TYPE= ACKB; TFIN=2001;TUN=301;FFIN=2001;FUN=201;CCH=801; CMOD=16

### EMERGENCY, x

X: extension qualifier depends on the master application

Extension Emergency call to 123456789 from mobile unit 301 on control channel 1:

MSG=MPT-INP; TYPE= ENERG,xxxx; TFIN=2001;FUN=301;CCH=801; CMOD=16; DIAL=123456789

Acknowledge

MSG=MPT-OUT; TYPE= ACKB,xxxx; TFIN=2001;TUN=301;CCH=801; CMOD=16

Xxxx= 8101 PSTN or 8102 PABX

Go to channel and make connection to module 2

MSG=MPT-OUT; TYPE= GTC,xxxx; TFIN=2001;TUN=301;CCH=801; CMOD=16; TCH=901; FMOD=2

### CANCEL

Information about Mobile unit 301 cancel a pending call on control channel

MSG=MPT-OUT; TYPE= CANCEL; TFIN=2001;TUN=201; FFIN=2001; FUN=301; CCH=801; CMOD=16

Acknowledge

No Acknowledge. The system automatically generate an ACK

### CANCEL, x

Information about Mobile unit 301 cancel a extension pending call on control channel

MSG=MPT-OUT; TYPE= CANCEL,9000; FFIN=2001;FUN=301;CCH=801;CMOD=16;

Acknowledge

No Acknowledge. The system automatically generate an ACK

### CON

Connection on traffic channel 1 module 17 to unit 201 from unit 301

MSG=MPT-OUT; TYPE= CON; TFIN=2001;TUN=201;FFIN=2001;FUN=301; CCH=801;CMOD=16;TCH=901;TMOD=17;FMOD=2

### PRESSEL

PRESSEL 1/0 on traffic channel 1 module 17 from unit 301

MSG=MPT-OUT; TYPE= PRESSEL, 1 or 0; FFIN=2001;FUN=301;TCH=901;TMOD=17

NACK, ERR=

System Rejections

NACK;ERR= No reply from called unit

NACK;ERR= Called unit rejects call

NACK;ERR= Called unit unavailable

NACK;ERR= System occupied

NACK;ERR= System overloaded

NACK;ERR= Invalid call

NACK;ERR= Control/traffic module error

NACK;ERR= Identity error

NACK;ERR= Connect rejected

### ACK specification:

Please note transmitting or receiving an ACK  to units TO and FRAM parameters shall / will bee swapped.

ACK	Accept - General

ACKB	Accept  - Called unit has accepted the call for call-back,

ACKI   Wait Acknowledge

ACKV Subscriber absent Acknowledge

ACKX Rejection invalid Acknowledge

ACKX,8185 Registration Rejection acknowledge

### Other examples

Example Module 2 want a speech connection to unit 302 and  my unit number is 301:

MSG=MPT-OUT;TYPE=CALL;MSGNO=12;FUN=302;TUN=302; CCH=801;FMOD=2

Com4500 uses the first free traffic channel for conversation. If you want to use a specific traffic channel you have to specify the channel number for example TCH=901

Example Transmit status 3 to unit 302 and  my unit number is 301:

MSG=MPT-OUT;TYPE= STATUS,3;MSGNO=13;FUN=302;TUN=302; CCH=801

CLEAR command without FMOD and only TCH=yyy will transmit clear on the traffic channel and keep the conversation running.

CLEAR command with FMOD=xxx and TCH=yyy will transmit clear on the traffic channel and shutdown conversation.

Using CALL without FMOD loaded will just check the reach ability for the MPT unit

(301) on the selected control channel.

MSG=MPT-OUT;TYPE= CALL;MSGNO=65;FUN=301;CCH=801

Response Message: The string can bee modified showing XCH=2 and the selected TMOD=2 for first available module.

### GET SETUP

Get setup command return a SETUP command from server

MSG=MPT-OUT; TYPE=GETSETUP; Command string

Command string: CH1=;MODE1=;TR1=

Response returns information about CH1,MODE1 and TR1

You want for example information about CH1=;MODE1=;TR1=;

MSG=MPT-OUT; TYPE=GETSETUP; CH1=;MODE1=;TR1=

Response

MSG=MPT-OUT; TYPE=GETSETUP;

DATA, CH1=801,1,16; MODE1=201,2,2,2,3; TR1=901,2,17

### SET SETUP

MSG=MPT-OUT; TYPE=SETSETUP; Command string

MSG=MPT-OUT; TYPE=SETSETUP; CH1=801,27,1

Response without fault

MSG=MPT-OUT; TYPE=SETSETUP; CH1=801,27,1

Response wit fault

MSG=MPT-OUT; TYPE=SETSETUP; CH1=801,27,1;ERR=text fault

Four commands identifying Control Channel 1 to 4

CH1=

CH2=

CH3=

CH4=

Code example for two control channel without locked site diversity

The list consist of 3 parameter

Channel reference number, Radio Frequency Channel number, Control Module number for site 1

Site               1

CH1=801,27,1

CH2=802,24,7

Command string: CH1=801,27,1;CH2=802,24,7

Control channel 1 (CH1=801,27,1)

System command channel reference number is 801 and the mobile radio use frequency channel 27 and Com4500 use local module is 1.

Code example for two control channel with locked site diversity

The list consist of 4 or more  (max 16 sites) parameter

Channel reference number, Radio Frequency Channel number, Control Module no. for site 1, Control Module no. for site 2, ……..  Control Module no. for site 16

Zero= no control channel/module on this site

Site               1 2 3 4 5

CH1=801,27,1,2,3,4,5

CH2=802,24,7,0,8,9,0

Command string: CH1=801,27,1,2,3,4,5;CH2=802,24,7,0,8,9,0

Control channel 1 (CH1=801,27,1,2,3,4,5)

System command channel reference number is 801 and the mobile radio use frequency channel 27 and Com4500 use local module is 1 for site 1, local module is 2 for site 2, local module is 3 for site 3 etc. building a locked site diversity control channel consisting of module 1,2,3,4,5

Control channel 2 (CH2=802,24,7,0,8,9,0)

System command channel reference number is 802 and the mobile radio use frequency channel 24 and Com4500 use local module is 7 for site 1, no local module on site 2, local module is 8 for site 3 etc. building a locked site diversity control channel consisting of module 7,0,8,9,0.

The diversity control channel 2 have no modules on site 2 and 5 .

Eight commands identifying traffic Channel 1 to 8

TR1=

TR2=

TR3=

TR4=

TR5=

TR6=

TR7=

TR8=

Code example for two control channel and two traffic channels without locked site diversity

All modules located on the same site(1)

The list consist of 3 parameter

Channel reference number, Radio Frequency Channel number, Control Module number for site 1

Site                1

CH1=801,27, 1

CH2=802,24, 7

Channel reference number, Radio Frequency Channel number, Traffic Module number for site 1

Site                1

TR1=901,38,22

TR2=902,39,23

Command string: CH1=801,27,1; CH2=802,24,7; TR1=901,38,22; TR2=902,39,23

Code example for two control channel and two traffic channels  with locked site diversity

Channel reference number, Radio Frequency Channel number, Control Module no. for site 1, Control Module no. for site 2, ……..  Control Module no. for site 16

Zero= no control channel/module on this site

Site                1  2  3  4  5

CH1=801,27, 1, 2, 3, 4, 5

CH2=802,24, 7, 0, 8, 4, 0

Channel reference number, Radio Frequency Channel number, Traffic Module no. for site 1, Traffic Module no. for site 2, ……..  Traffic Module no. for site 16

Zero= no control channel/module on this site

Site                1   2   3   4  5

TR1=901,38,21,22,23,24,25

TR2=902,39,27, 0,28,29, 0

Command string: CH1=801,27,1,2,3,4,5; CH2=802,24,7,0,8,4,0;

TR1=901,38,21,22,23,24,25; TR2=902,39,27,0,28,29,0;

Commands for DEFAULT Setup numbers on control channel 1 to 4

DEF1=FFIN=2001,FUN=201;

DEF2=

DEF3=

DEF4=

DEF1= FFIN=xxxx,FUN=yyy;

DEF1= FFIN=2001,FUN=201;

FFIN= 	From Fleet number 2001 to 6050

FUN=  	From unit number  200 to 899 or (20 to 89 for two digits)

Command for mode Setup, Control Channel 1..4

The list consist of 5 parameters:

NP=	    Number prefix for channel (200 to 327 default 201)

CCHTIME=  Time slot 1..3 control channel use CCTIME * 110 ms (default 2)

CCHPAUSE= Pause slot 1..3 control channel use CCPAUSE * 110 ms (default 2)

CCHVOTE=  Voting slot 1..10 ch channel voting CCHVOTE * 110 ms (default 2)

CCHLET=   LET time for control channel transmitter * 10 ms (default 3)

MODE1=NP,CCHTIME,CCHPAUSE,CCHVOTE,CCHLET

MODE2=

MODE3=

MODE4=

Example:

Command string: MODE1=201,2,2,2,3

Commands for fleet Setup

The list consist of 4 parameter

Fleet1= Min individual number, Size of fleet, Fleet number, Fleet offset

Fleet number= (Min individual number Div 2) + 2000

Example Fleet number = 2 Div 2 + 2000 = 2001

Fleet offset = 20 for 2 digits or 200 for 3 digits units numbers

Fleet offset = 90 for 2 digits or 900 for 3 digits group units numbers

Command string: FLEET1=2,700,2001,200

FLEET2=

FLEET3=

FLEET4=

# FMS command format for COM4500-TSC

FUNKMELDESYSTEM or BOS radio system

Only status calls and text calls op to 99 char are supported.

## Channel Limitations.

Only modules setup for FMS tone can use the FMS calling system

The BOS radio system can not be used with diversity and Co channels.

Single tone 1750 Hz and 2135 Hz receiving  is not supported

## Speech connections

Use the normal EXTCONNECT without tone signalling or EXTREPEAT to make speech  connections between the operator and the radio module

## Application Server(master) -> Com4500-TSC:

STATUS:	Status call

STEXT:	Short data call

ACK:		Acknowledge

TONEACK:	625 Hz caustic Acknowledge to module (only CMOD shall be loaded )

TON1750:	Transmit Tone 1750 Hz (only CMOD shall be loaded)

TON2135:	Transmit Tone 2135 Hz (only CMOD shall be loaded)

## Com4500-TSC -> Application Server (master):

STATUS:	Status call

STEXT:	Short data call

ACK:		Acknowledge

TON1750:	Tone 1750 Hz received (only CMOD will be loaded)

TON2135:	Tone 2135 Hz received (only CMOD will be loaded)

## Command format:

Mandatory commands can be defined and loaded from the P45453.ini file.

Commands overwrite values defined in P45453.INI

BOS=		; Number  (range 1 to 15 )		(mandatory or defined in P45453.INI)

LAND=	; Number  (range 0 to 15 )		(mandatory or defined in P45453.INI)

ORT=		; Number  (range 00 to 99  )		(mandatory or defined in P45453.INI)

STAT=	; Number  (range 0 to 15 ) 		(mandatory or defined in P45453.INI)

ID=		; User ID  (range 0000 to 9999 )	(mandatory or defined in P45453.INI)

BK=		; Number  (range 0 to 1 ) 		(mandatory or defined in P45453.INI)

TK=		; Number  (range 0 to 3 ) 		(mandatory or defined in P45453.INI)

CMOD=	; Module number (range 1 to 512)        (mandatory )

MSG=							(mandatory)

STATUS

STEXT,HELLO WORLD                                    	(Text “Hello world” to unit)

ACK, x 					(see specification)

TONEACK	(only CMOD is used)

TON1750	(only CMOD is used)

TON2135	(only CMOD is used)

PS. The message identifier “MSG=” must by the last identifier in the string.

## Command from Application Server (master)

### STATUS

Transmitting status 3 to mobile 1234 on module 18.

If acknowledge isn’t received from mobile unit the status call is transmitted once

BOS=1,LAND=4,ORT=33,ID=1234,STAT=3,BK=1,TK=3,CMOD=18,MSG=STATUS

### STEXT

Transmitting text to mobile 1234 on module 18

BOS=1,LAND=4,ORT=33,ID=1234,CMOD=18,MSG=STEXT, Hello world

### ACK

Transmitting ACK status 15 to mobile 1234 on module 18 once

BOS=1,LAND=4,ORT=33,ID=1234,STAT=15,BK=1,TK=3,CMOD=18,MSG=ACK

### TONEACK

Acoustic tone 625 Hz (400 ms) on module 18

CMOD=18,MSG=TONEACK

### TON1750

Calling tone 1750 Hz (1000ms) on module 18

CMOD=18,MSG=TON1750

### TON2135

Calling tone 2135 Hz (1000ms) on module 18

CMOD=18,MSG=TON2135

## Command from Com4500 to Application Server (master)

### STATUS

Receiving status 3 from mobile 1234 on module 18

BOS=1,LAND=4,ORT=33,ID=1234,STAT=3,BK=1,TK=3,CMOD=18,MSG=STATUS

### TON1750

Receiving calling tone 1750 Hz on module 18

CMOD=18,MSG=TON1750

### TON2135

Receiving calling tone 2135 Hz on module 18

CMOD=18,MSG=TON2135

## ACK specification:

ACK	;Accept - General

ACK,0	;Accept – Text transmission timeout

ACK,1	;Reject – No reply from called unit

ACK,2	;Reject – Called unit rejects call

ACK,3	;Reject – Called unit unavailable

ACK,4	;Reject – System occupied

ACK,5	;Reject – System overloaded

ACK,6	;Reject – Invalid call

ACK,7	;Reject – Module error

ACK,8	;Reject – Identity error

ACK,9	;Reject – No connection to rack

FMS REQ.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 255 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

Comma separated text identifying the call

The message identifier “MSG=” must by the last identifier in the string

Example Status 5 to unit 2011 on module 2:

BOS=1,LAND=2,ORT=32, ID=2011,STAT=5,BK=0,TK=3 CMOD=2,MSG=STATUS

BOS=1	(BOS-KENNUNG 1)

LAND=2	(LAND-KENNUNG 2)

ORT=32	(ORT-KENNUNG 32)

ID=2011	(FARZEUG-KENNUNG 2011)

STAT=5    (STATUS 5)

BK=0	(BAUSTUFE KENNUNG 1 )

TK=3	(TAKTISCHE KURZINFORMATION 3 )

CMOD=2  (use internal FMS module 2)

MSG=STATUS (Message status)

FMS Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Number | Unsigned Short | 2 | 0 |  | Not used yet |
| 4 | Error Text | Char | 80 | Spaces |  | Text |

- ID.

Always zero

- MODE

Always zero.

- Number

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

## Set FMS setup.

SET FMS Setup.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Command Message | Char | 255 | Spaces |  | Text |

- ID.

Always zero

- MODE

Always zero.

- Command Message

Commands are separated by space or “;” and parameters are comma separated text

You can combine one or more commands in the string

Commands for optional Setup numbers

BOS=

LAND=

ORT=

ID=

BK=

TK=

Command for mode Setup for FMS  Channels (NOT SUPPORTED)

The list consist of 4 parameters:

CCHTIME=  	Time slot channel use CCTIME * 110 ms (default 1)

CCHPAUSE= 	TX pause between calls / wait ACK (default 10 = 1000 ms)

CCHVOTE=	Voting timeout  (default 2) not supported in the system

CCHLET=		LET time for transmitter * 10 ms (default 20)

MODE=		CCHTIME,CCHPAUSE,CCHVOTE,CCHLET

Example for default values:

MODE=1,10,2,20

Set FMS setup Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Number | Unsigned Short | 2 | 0 |  | Not used yet |
| 4 | Error Text | Char | 80 | Spaces |  | Text |

- ID.

Always zero

- MODE

Always zero.

- Number

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

# SYS CMD

## SYS CMD.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- Message

MSG=COMMAND, parameter 1, parameter 2 ….. parameter n

## SYS-CON command (App-server -> Winser)

MSG=	SYS-CON

TYPE= 	CON-CONF		[FMOD, TMOD], [FMOD, TMOD, DIAL]	[LNK]

CON-CONFX		[FMOD, TMOD], [FMOD, TMOD, DIAL]	[LNK]

CON-SINGLE		[FMOD, TMOD], [FMOD, TMOD, DIAL]	[LNK]

CON-SINGLEX	[FMOD, TMOD], [FMOD, TMOD, DIAL]	[LNK]

CON-SPEAK		[FMOD, TMOD]

CON-LISTEN		[FMOD, TMOD]

JOIN			[FMOD, TMOD], [XCH, TMOD]		[LNK]

HOLD			[TMOD] , [XCH, TMOD]

PARK			[TMOD] , [XCH, TMOD]

HOOK			[TMOD] , [TMOD, MODE], [TMOD, DIAL],

[TMOD, DIAL, DATA, ANUM]

REMOVE		[FMOD, TMOD], [TMOD], [XCH] , [XCH, TMOD]

[LNK]

DISCONNECT			[TMOD]

DISCONNECTCONFIRM	[TMOD]

MON-ADD		[FMOD, TMOD]				[LNK]

MON-ADDX		[FMOD, TMOD]				[LNK]

MON-ADDX2		[FMOD, TMOD]				[LNK]

MON-REMOVE	[FMOD, TMOD], [FMOD]			[LNK]

MON-SETUP		[FMOD,TMOD]				[LNK]

MON-LEVEL		[FMOD, TMOD, LEVEL]

MUTE			[TMOD, LEVEL]

PLAY-VOICE		[TMOD, TRACK],

PLAY-SOUND		[FMOD, TMOD, TRACK]

PLAY–MUSIC		[FMOD, TMOD]

PLAY–STOP		[TMOD]

DELETE-WAVFILE	[TRACK]

RECORD-SOUND	[FMOD, TMOD, TRACK]

RECORD-STOP	[TMOD, TRACK]

FMOD=	[Module1]

TMOD=	[Module1] or [Module1, Module2, Module3,…]

XCH=		[Talk channel1] or [Talk channel1, Talk channel2, Talk channel3,…]

LNK=		[LinkSupport on: S], [LinkSupport off: 0], [LinkIndex: 1..128]

DIAL=		[Digittype, Digits]

Digittype: CCIR, ZVEI, MPT, DTMF, DIAL, SPEC, AP, EIA, FMS, TETRA

Digits:       0123456789ABCDEF*#

i.e. [CCIR,12345], [DTMF,12345678;ANUM=23456]

Special separator for dial

i.e. [TETRA,12345+67890] for ToID=12345 and FromID=67890 and separator[+]

i.e. [CCIR,52345+57890] for ToID=52345 and FromID=57890 and separator[+]

TIMEOUTS=   x, y, z, v only supported by the HOOK command

x = Let time x 10 ms.		0 = default timing;

y=  Tone timing x 10 ms	0 = default timing

z= Pause timing x 10 ms only DTMF else zero

v= Wait timing x 100 ms (DTMF) or

Long tone timing x 100ms	0 = default timing

Tone systems: CCIR, ZWEI, DTMF and EIA

TIMEOUT missing or empty the system used default timing.

NOKEY=         <> 0 = Key disabled on module during this conversation

Only valid using  [CON_CONF| CON-CONFX| CON-SINGLE|

CON-SINGLEX | CON-SPEAK| CON-LISTEN| JOIN]

KEYON=         <> 0 = Key on module(s) for a time specified by TIME=xx.  (xx * 0,1 sec)

Only valid using  [CON-CONF| CON-CONFX| CON-SINGLE|

CON-SINGLEX | CON-SPEAK| CON-LISTEN| JOIN]

Example: Key on module 8 for 2,0 sec.

MSG=SYS-CON;TYPE=CON-CONF;FMOD=2;TMOD=8;KEYON=8;TIME=20

MODE=	[HOOKOFF | REJECT | CLEAR | ALERT | PROCEED] only ISDN module HM815

LEVEL=	[Mon-level: 0..63], [Mute: 1..255]

TRACK=	[Track: 1..255 or path], [Repeat: 1..255]

DATA=	MyText[1..160] or MyData[1..160]

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

### XCH support

Activating a new AF command the response will add a XCH=VV parameter, where VV is the actual conference number used in Winser32.exe.

This value can be used in more sophisticated CON-CONF, CON-CONF X, CON-SINGLE, CON-SINGLEX, JOIN, REMOVE ,HOLD and PARK commands.

### CON-CONX section

These commands support AF and dialling with one FMOD as reference module and one TMOD as subscriber modules with or without link support to another system.

Normal TMOD=9 for a specific module, but you can get first free module out of several by using TMOD=*9,10,11 the response shows the selected module

TMOD=*9 the system will reject the call if module 9 is occupied

TMOD=9 the system will use module 9 even it is occupied by another user

CON-CONF:

Conference between two or more modules with or without dialling.

If the first module (the reference) is removed or disconnected the hole conference is removed

Command:

MSG=SYS-CON;FMOD=1; TMOD=2;TYPE=CON-CONF

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF; XCH=3

Conference between two or more modules with dialling.

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;DIAL=DTMF,12345

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;DIAL=DTMF,12345;XCH=3

Conference between two or more modules with dialling and fist free module.

MSG=SYS-CON;FMOD=1;TMOD=*2,3,4;TYPE=CON-CONF;DIAL=DTMF,12345

Response shows module 3 and conference number 2 selected

MSG=SYS-CON;FMOD=1;TMOD=3;TYPE=CON-CONF;DIAL=DTMF,12345;XCH=2

CON-CONFX:

Conference between two or more modules with or without dialling.

If the first module (the reference) is removed the conference will still exist with the remaining modules.

Command:

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONFX

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONFX;XCH=3

Conference between two or more modules without dialling.

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONFX;DIAL=DTMF,12345

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONFX;DIAL=DTMF,12345;XCH=3

CON-SINGLE:

Single include mode  with or without  dialling.

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE= CON-SINGLE;DIAL=DTMF,12345

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE= CON-SINGLE;DIAL=DTMF,12345;XCH=3

CON-SINGLEX:

Special Single X include mode  with or without dialling.

Module 1 in SINGLEX mode with module 2. AF from all other modules using module 2 will bee transmitted to module 1.

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE= CON-SINGLEX;DIAL=DTMF,12345

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE= CON-SINGLEX;DIAL=DTMF,12345;XCH=3

Link support:

Command with Link support to another system:

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;LNK=S

Response Link number 1 and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;LNK=1;XCH=3

Command with Link support off:

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;LNK=0

Response and conference number 3 selected

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=CON-CONF;XCH=3

Link index Command  to another system:

MSG=SYS-CON;LNK=1;TMOD=3;TYPE=CON-CONF

Response and conference number 2 selected

MSG=SYS-CON;LNK=1;TMOD=3;TYPE=CON-CONF;XCH=2

Remove link index 1 to the other system

MSG=SYS-CON;LNK=1;TYPE=REMOVE

### JOIN

Join an existing conference using reference module or conference number as reference.

Command:

MSG=SYS-CON;FMOD=1;TMOD=2,3;TYPE=JOIN

Command:

MSG=SYS-CON;XCH=2;TMOD=2,3;TYPE=JOIN

### HOLD and PARK

HOLD holds a module in your conference. Park free a module from a conference and get a new separate conference number making it possible for others to move the module to there conference.

MSG=SYS-CON;TMOD=2;TYPE=HOLD;XCH=4

Hold module 2 in my conference number 4

MSG=SYS-CON;TMOD=2;TYPE=PARK

Park module 2. Removing module 2 from all conferences

### HOOK

Dialling on a specific module. The module can bee in conversation or not.

MSG=SYS-CON;TMOD=2;TYPE=HOOK;DIAL=DTMF,12345678

MSG=SYS-CON;TMOD=2;TYPE=HOOK;DIAL=DTMF,12345678;ANUM=123456

MSG=SYS-CON;TMOD=3;TYPE=HOOK;DIAL=CCIR,12345

MSG=SYS-CON;TMOD=4;TYPE=HOOK;DIAL=MPT,123456;DATA=Hello world

Dialling on a specific module with timeouts (300ms let time)

MSG=SYS-CON;TMOD=3;TYPE=HOOK;DIAL=CCIR,12345;TIMEOUTS=30,0,0,0

Answer a ringing with alerting from application server and hook off

MSG=SYS-CON;TMOD=4;TYPE=HOOK;MODE=ALERT

MSG=SYS-CON;TMOD=4;TYPE=HOOK;MODE=HOOKOFF

Answer a ringing with hook off and auto alert in WINSER server

MSG=SYS-CON;TMOD=4;TYPE=HOOK;MODE=HOOKOFF

### REMOVE

The command removes AF with FMOD as one reference module and TMOD as one or more subscriber modules with or without link support to another system.

A REMOVE command can remove a module or conference in different ways.

Remove module 1 from all conference / single in the system

MSG=SYS-CON;FMOD=1;TYPE=REMOVE

Remove module 2 from conference / single using module 1 as reference in the system

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=REMOVE

Remove module 1 only from  conference number 3

MSG=SYS-CON;FMOD=1;TYPE=REMOVE;XCH=3

Remove the hole conference  with conference number 3

MSG=SYS-CON;TYPE=REMOVE;XCH=3

### DISCONNECT

Disconnect module 1

MSG=SYS-CON;FMOD=1;TYPE=DISCONNECT

### DISCONNECTCONFIRM

Finally Disconnect emergency receiver module 16

MSG=SYS-CON;TMOD=16;TYPE=DISCONNECTCONFIRM

### MON-XXXX section

These monitor commands support AF only with FMOD as one reference module and TMOD as one or more subscriber modules with or without link support to another system.

MON-ADD:

MSG=SYS-CON;FMOD=1;TMOD=2,3;TYPE=MON-ADD

Patch module 2 an 3 to Module 1 for monitoring

MON-ADDX:

MSG=SYS-CON;FMOD=1;TMOD=2,3;TYPE=MON-ADDX

Patch module 2 an 3 to Module 1 for monitoring.

AF from all other modules using module 2 ,3  will bee transmitted to module 1.

MON-REMOVE:

MSG=SYS-CON;FMOD=1;TMOD=2;TYPE=MON-REMOVE

Remove monitoring 2 from reference Module 1

MON-SETUP:

Monitor tape output following a specific module (typically an operator).

Use Module 3 as tape output  following module 1. Every time module 1 is active the tape output is active. Automatic remove of tape when module 1 is inactive.

Command:

MSG=SYS-CON;FMOD=3;TMOD=1;TYPE=MON-SETUP

MON-LEVEL :

Standard MON-OPEN with level control on a monitor modules

Value [0…63] 63 = decrease level with -63dB

MSG=SYS-CON;FMOD=1;TMOD=3,4,5;TYPE=MON-LEVEL;LEVEL=10

### MUTE

The mute/ gain command  is only active on HM808/1 cards in Local AGC or TRC mode!

The command can change TX level on the module.

Values: 0 = 0dBm, 50 = -5 dBm, 100 = -10 dBm and  255 = - 25.5 dBm

MSG=SYS-CON;FMOD=1;TMOD=3;TYPE=MUTE;LEVEL=100

### PLAY-XXXX

Play HM801/3 voice 1 on module 3

MSG=SYS-CON;TMOD=3;TYPE=PLAY-VOICE;TRACK=1

Play SoundBlaster file xxxx.wav on module 3. (SoundBlaster is connected to module2)

Specified path and file

MSG=SYS-CON;FMOD=2;TMOD=3;TYPE=PLAY-SOUND;TRACK=C:\XXPATH\ XX.WAV

If you only specify the file name the path will bee the default the voice directory.

MSG=SYS-CON;FMOD=2;TMOD=3;TYPE=PLAY-SOUND;TRACK= XX.WAV

Stop any voice or SoundBlaster on module 3

MSG=SYS-CON;TMOD=3;TYPE=PLAY-STOP

### RECORD-SOUND

Record a SoundBlaster file xxxx.wav  using module 3 as input. (SoundBlaster is connected to module2)

Specified path and file

MSG=SYS-CON;FMOD=2;TMOD=3;TYPE=RECORD-SOUND;TRACK=C:\XXPATH\ XX.WAV

If you only specify the file name the path will bee the default the voice directory.

MSG=SYS-CON;FMOD=2;TMOD=3;TYPE=RECORD-SOUND;TRACK= XX.WAV

### RECORD-STOP

Stop recording a SoundBlaster file xxxx.wav  using module 3

MSG=SYS-CON;TMOD=3;TYPE=RECORD-STOP;TRACK= XX.WAV

## SYS-CON command: (Winser -> App-server)

MSG=	SYS-CON

TYPE= 	PLAY–STOPPED,PLAY-FAULT,RECORD-FAULT	[FMOD]

FMOD=	[Module1]

MSG=SYS-CON;FMOD=3;TYPE=PLAY-STOPPED

Information about voice or SoundBlaster is stopped on module 3

MSG=SYS-CON;FMOD=3;TYPE=PLAY-FAULT

MSG=SYS-CON;FMOD=3;TYPE=RECORD-FAULT

## SYS-OUT command: (App-server ->Winser)

MSG=	SYS-OUT

TYPE= 	KEY,n				n: 0 = off. 1 = on

EMERG-ACCEPT,n		n: 0 = off. 1 = on

RINGINGTONE,n		n: 0 = off. 1 = on

RXAUDIO,n			n: 0 = off. 1 = on

RBUTTON,n			n: 0 = off. 1 = on

RINGACTION,n		n: 0 = off. 1 = on

DING,n				n: 0 = off. 1 = on

ALARMRINGACTION,n	n: 0 = off. 1 = on

RELAY, OUT=a,n	a: output 1..64,	n: 0=off. 1 = on

TESTTONE,	MODE=x,	x: 0=off. 1=on. 2=continuously

FREQ=x,	x: 0=Frequency, 1=Dual frequency

TIME1=xxxx,	0 to FFFF hex in steps of 10 ms

TIME2=xxxx,	0 to FFFF hex in steps of 10 ms

TONE1=xxxx,	300 to 3400 using frequency in Hz

TONE2=xxxx,	0 to 3400 using frequency in Hz

LEVEL=x	x: 0= -16dBm 1=-13dBm 2=-10dBm

SETMPTRX	ACK=n,	n: 0 = no auto MPT-acknowledge,  (IHM text only)

1 = use auto MPT-acknowledge

COM53	Com53,”command” ie. Com53,”CAL=SPE,vvvv-yyyy;TYP=NOR” 		COM53	Com53,”command” ie. Com53,”CAL=MPT,vvyyvvyyvvyy”

(vv or yy = Hex value of MPT byte – max 60 bytes)

HM817 protocol

TETRA-ALERT	Tetra alerting

TETRA-ACCEPT	Tetra call accepted

TETRA-REJECT	Tetra call rejected

TETRA-DATA		Tetra data call

TLREQ			TL request

TLREQ	,	GPS location control

TRC=		?LOC		Request immediate GPS location.

?TRC_X_Y	Trigged GPS location. X = Interval in minutes. Y = Number of pos.

TMOD=	[Module1]

DATA=

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

MSG=SYS-OUT;TMOD=1;TYPE=KEY,1

MSG=SYS-OUT;TMOD=; TYPE=KEY,0

MSG=SYS-OUT;TMOD=1;TYPE= EMERG-ACCEPT,1

MSG=SYS-OUT;TMOD=; TYPE= EMERG-ACCEPT,0

MSG=SYS-OUT; TMOD=1;TYPE=DING,1

MSG=SYS-OUT;TMOD=1;TYPE=DING,0

MSG=SYS-OUT;TYPE=RELAY;OUT=2,1

MSG=SYS-OUT;TYPE=RELAY;OUT=2,0

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1234-5670;TYP=TYF”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=CCI,12345”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CALL=MPT,112233445566”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=CC,12345”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,” CAL=POC,12345,6789,1456”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,” CAL=POC,12345,6789,1456;TXT=”Hello world””

MSG= SYS-OUT;TYPE=TESTTONE;MODE=1;FREQ=0;TIME1=100;TIME2=50;

TONE1=1000;TONE2=2200;LEVEL=0;TMOD=1,23,37

MSG=SYS-OUT;TMOD=1;TYPE=SETMPTRX;ACK=1 (IHM text only not standard MPT)

MSG=SYS-OUT;TMOD=1;TYPE=TLREQ;DIAL=TETRA,1234-5678;TRC=?LOC

## SYS-EMERGENCY command: (App-server ->Winser)

Emergency receiver HM807/2 or HM807/3

MSG=	SYS-EMERGENCY

TYPE=		EMERGTX

DIALTYPE:	[DTMF | FSK | CONFIG]

TMOD=	[Module]

DATA= 	[pair of hex values: 11 = $11, 22=$22, 01=$01]

MSG=SYS-EMERGENCY; TYPE= EMERGTX; TMOD=27;DIALTYPE=DTMF; DATA=1122112211221122

MSG=SYS-EMERGTX; TYPE= EMERGTX; TMOD=27;DIALTYPE=FSK; DATA=1122112211221122

MSG=SYS-EMERGTX; TYPE= EMERGTX; TMOD=27;DIALTYPE=CONFIG; DATA=1122112211221122

### Com53 output call commands

CAL= dial-type[CCI, ZVE, DTM, SPE, POC, MPT,SPC], dial number[0..9];Optional commands

CCI: CCIR tone system

ZVE: ZWEI tone system

DTM: DTMF tone system

POC: POCSAG signalling (1200 or 2400 baud)

MPT: MPT signalling (1200 baud)

SPC: Special signalling

SPE: SPEEDA signalling

Optional commands

TXE=YES transmit TX done from COM53 unit [CCI, ZVE, DTM, SPE, POC, MPT]

TXT=”My new Text” transmit this text on COM53 unit [SPE, POC]

SYN= 0,1 on COM53 unit [MPT] 1= SYNT and 0= SYNC (default)

TON= tone duration in ms on COM53 unit [SPC]

LEV= Tone level [10,13,16] dBm on COM53 unit [SPC]

Call CCIR, ZWEI and DTMF 12345 on module 27 and do not transmit TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=CCI,12345”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=ZVE,12345”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=DTM,12345”

Call CCIR, ZWEI and DTMF number 12345 on module 27 and transmit TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=CCI,12345;TXE=YES”

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=CCI”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=ZVE,12345;TXE=YES”

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=ZVE”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=DTM,12345;TXE=YES”

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=DTM”

SPC

Transmit 1000 Hz tone on module 27. Tone duration 2500 ms and level –10dBm

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPC,1000;TON=2500;LEV=10; TXE=YES”

Transmit 1000 Hz tone on module 27. Tone duration 10000 ms and level –16dBm

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPC,1000;TON=10000;LEV=16; TXE=YES”

POCSAG

Call POCSAG number 12345 on module 27 without text and do not transmit TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=POC,12345”

Call POCSAG numbers 12345, 6789 and 1456 on module 27 without text and transmit TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=POC,12345,6789,1456;TXE=YES”

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=POC”

Call POCSAG numbers 12345, 6789 and 1456 on module 27 with text and  transmit TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=POC,12345,6789,1456;TXE=YES; TXT= ”Hello world””

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=POC”

MPT

Call MPT digits 0,1,2,3,4,5. Each byte value must be converted ASCII hex

MPT can transmit from 6 up to 30 digits (string length from 12 to 60 hex char)

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=MPT,000102030405;TXE=YES;SYN=1”

TX done on COM53 unit

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=MPT”

Call MPT digits 255,32,33,12,3,4. Each byte value must be converted ASCII hex

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=MPT,FF20210C0304”

### Com53 output  commands

Com53 has 8 outputs and a key (K)

Capital letters indicates active outputs. Small letters indicates inactive outputs

OUT= A, B, C, D, e, f, g, h , K

Key  module 27 on COM53 unit

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”OUT=K”

Key off module 27 on COM53 unit

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”OUT=k”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”OUT= A, B, C, D, e, f, g, h”

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”OUT= A, b, C, D, e, f, g, h”

### Com53 internet AF connection OPEN/ CLOSE  commands

Open internet AF connection on squelch active from COM53 to HM817/1 (Server)

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”SET=CON;AF=YES'”

Close internet AF connection from COM53 to HM817/1 (Server)

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”SET=CON;AF=NO'”

### SPEEDA commands

CAL	Call to and from a radio.

CON	Connection with conversation.

REL	Release conversation.

LON	Logon received from radio.

LOF	Log Off received from radio.

POL	Polling a radio with or without GPS

ACK	Acknowledge to and from a radio with or without GPS

NAK	No acknowledge from a radio.

UNR	Radio has no registration .

Options

TYP	[NOR,TYF,TXT,GRP,ALL]. Commands [CAL]

CH	Channel number. Commands [CAL,CON,UNR]

RET	[YES,NO] answer from radio. YES is default. Commands [CAL]

DEL	[DISP,QUE] delete information in display or queue. Commands [REL]

TXE	[YES]	transmit TX done. Commands [CAL,POL]

TXT	“Hello world” . Commands [CAL]

CNT	number of times making the call. Default = 1. . Commands [CAL]

RSSI	[0 – 15] . Commands [CAL,ACK,CON,LON,UNR]

GPS=	1_N12.20.43,0_W24.40.7,0_19.11.2004_09:31:25_000km/h_0deg

Latitude,       Longitude,    Date,             Time,       Speed,     Direction .

Commands [CAL,CON,ACK,LON]

Latitude: 	_N or _S, _degrees, minutes, seconds, second-fractions

Longitude: 	_E or _W, _degrees, minutes, seconds, second-fractions

Date:		_Date, month, year

Time:		_Hour, minute, second

Speed:		_xxxkm/h.  (000-999 km/h):

Direction:	_xdeg	      (0-360 deg)

TYFON-Calls:

Normal TYFON on channel 10

MSG=SYS-OUT;TMOD=27;TYPE=COM53,“CAL=SPE,1234-5678;TYP=TYF;CH=10”

Group TYFON on channel 10

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1111-5678,2222-5678; TYP=TYF,GRP;CH=10”

All TYFON on channel 10

MSG=SYS-OUT;TMOD=27;TYPE=COM53,“CAL=SPE,9999-5678;TYP=TYF,ALL;CH=10”

All TYFON on channel 10 with TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,“CAL=SPE,9999-5678;TYP=TYF,ALL;CH=10;

TXE=YES”

GROUP Calls:

Group call on channel 10 with Acknowledge from radios

MSG=SYS-OUT;TMOD=27;TYPE=COM53,“CAL=SPE,1111-5678,2222-5678;TYP=GRP;CH=10”

Group call on channel 10 without Acknowledge from radios

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1111-5678,2222-5678;TYP=GRP;CH=10; RET=NO”

Group call on channel 10 without Acknowledge from radios and TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1111-5678,2222-5678;TYP=GRP;CH=10; RET=NO;TXE=YES”

TEXT Calls:

Normal text call

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1234-5678;TYP=TXT;TXT=”Hello””

Text group call with Acknowledge from radios

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1111-5678,2222-5678;TYP=TXT,GRP; TXT=”Hello”

Text group call without Acknowledge from radios

MSG=SYS-OUT;TMOD=27;TYPE=COM53,“CAL=SPE,1111-5678,2222-5678;TYP=TXT,GRP; RET=NO;TXT=”Hello””

Text group call without Acknowledge from radios and TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1111-5678,2222-5678;TYP=TXT,GRP; RET=NO;TXE=YES;TXT=”Hello”

Text All call always without Acknowledge from radios and TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53, “CAL=SPE,9999-5678;TYP=TXT,ALL; TXT=”Hello””

Text All call always without Acknowledge from radios and TX done

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,9999-5678;TYP=TXT,ALL; TXE=YES;TXT=”Hello””

POLL Calls:

Logon call without GPS information on a running system

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”POL=SPE,1234-5678;GPS=NO”

Logon call with GPS information on a running system

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”POL=SPE,1234-5678;GPS=YES”

Logon call without GPS information on ID first time after power up

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”POL=SPE,1234-5678;GPS=NO,ID”

Logon call with GPS information on ID first time after power up

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”POL=SPE,1234-5678;GPS=YES,ID”

INCOMING calls

Call to 5678 from 1234 with or without RSSI information

MSG=SYS-INP;FMOD=27;TYPE=COM53,“CAL=SPE,5678-1234;RSSI=10;

Call to 5678 from 1234 with or without Channel, RSSI, GPS information

MSG=SYS-INP;FMOD=27;TYPE=COM53,“CAL=SPE,5678-1234;CH=10;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

Status 6 call to 5678 from 1234 with or without Channel, RSSI, GPS information

MSG=SYS-INP;FMOD=27;TYPE=COM53,“CAL=SPE,5678-1234;TYP=STA;STA=6; CH=10;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

CONNECT Call

Radio wants connect (Driver ready for conversation after a call)

MSG=SYS-INP;FMOD=27;TYPE=COM53,“CON=SPE, 5678-1234;CH=10;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

RELEASE-Call:

Release conversation

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”REL=SPE,1234-5678”

Release conversation and remove call from display in radio

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”REL=SPE,1234-5678;DEL=DISP”

Release conversation and remove call from queue in radio

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”REL=SPE,1234-5678;DEL=QUE”

ACKNOWLEDGE:

Acknowledge from radio with or without RSSI and GPS

MSG=SYS-INP;FMOD=27;TYPE=COM53,“ACK=SPE,5678-1234;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

LOGON

Logon from radio with or without RSSI and GPS

MSG=SYS-INP;FMOD=27;TYPE=COM53,“LON=SPE,5678-1234;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

LOG OFF

Log off from radio with or without RSSI and GPS

MSG=SYS-INP;FMOD=27;TYPE=COM53,“LOF=SPE,5678-1234;RSSI=10; GPS=”1_N55.44.15,6_E12.28.57,4_27.02.2006_12:35:36_000km/h_0deg””

Number of times transmitting the call:

Transmit the call one time on COM53 (default)

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1234-5678;TYP=NOR;CH=10”

Transmit the call two times on COM53 (default)

MSG=SYS-OUT;TMOD=27;TYPE=COM53,”CAL=SPE,1234-5678;TYP=NOR;CH=10;CNT=2”

No registration for the moment:

Radio 1234 can not be called available for calls or polling the moment. Will be located on channel 98

MSG=SYS-INP;FMOD=27;TYPE=COM53,“UNR=SPE, 5678-1234;CH=98”

## SYS-INP command (Winser -> App-server)

MSG=	SYS-INP

TYPE= 	RING                              [Ringing from module]

RING-EMERG               [Emergency ringing from module]

CALL                             [Call from module]

CALL-EMERG              [Emergency call from module]

DISCONNECT

DISCONNECTEMERGENCY

MPTTEXT

TETRA-ALERT	Tetra alerting

TETRA-ACCEPT	Tetra call accepted

TETRA-REJECT	Tetra call rejected

TETRA-DATA		Tetra data call

GPSI			[Immediate GPS information]

GPST			[Trigged GPS information]

GPSU			[Unsolicited GPS information]

TXCOMPLETE	[DIAL=MPT, “ID number”  (IHM text only)]

TXBUSY	             [Tone TX buffer full on hardware module.

Info frame No response from master]

KEY,n			n: 0=off. 1 = on

SQUELCH,n		n: 0=off. 1 = on

HOOK,n		n: 0=off. 1 = on

KEYSTATUS,n	n: 0=off. 1 = on

TXFINISH, TX=x	x: CCIR, ZVEI, MPT ,DTMF, DIAL,SPEC,AP,EIA,FMS

REPLY, TONE=x,a	x: CCIR, ZVEI, MPT, DTMF, DIAL,SPEC,AP,EIA,FMS

a: tone 0..F

ERROR, ERR=a,n	a: error 1..16, 	n: 0=off. 1 = on

OPTO, INP=a,n	a: input 1..64,	n: 0=off. 1 = on

COM53	Com53,”command” ie. COM53,”ACK=SPE,vvvv-yyyy”

COM53	Com53,”command” ie. Com53,”CAL=MPT,vvyyvvyyvvyy”

(vv or yy = Hex value of MPT byte – max 60 bytes)

(HM817 protocol)

FMOD=	[Module1]

DIAL=		[Digittype, Digits]

Digittype: CCIR, ZVEI, MPT, DTMF, DIAL, SPEC, AP, EIA, FMS

Digits:       0123456789ABCDEF*#

ie [DIAL=CCIR,12345], [DIAL=DTMF,A12345678,B11111111]

Special separator for dial

i.e. [TETRA,12345-67890] for ToID=12345 and FromID=67890 and separator[-]

i.e. [CCIR,52345-57890] for ToID=52345 and FromID=57890 and separator[-]

RSSI=		[level 0..15]

BUSY=		[0..1] 0= free and 1=Busy. (TYPE=TXBUSY;BUSY=1)

RID=		[Request ID (TETRA GPS information)]

DATAREF=	[Reference number for TETRA SDS call]

DATA=	MyText[1..160] or MyData[1..160]  (IHM text only)

GPS=		1_N12.20.43,0_W24.40.7,0_19.11.2004_09:31:25_000km/h_0deg

Latitude,       Longitude,    Date,             Time,       Speed,     Direction

Latitude: 	_N or _S, _degrees, minutes, seconds, second-fractions

Longitude: 	_E or _W, _degrees ,minutes, seconds, second-fractions

Date:		_Date, month, year

Time:		_Hour, minute, second

Speed:		_xxxkm/h.  (000-999 km/h):

Direction:	_xdeg	      (0-360 deg)

Commands are build of keywords separated by semicolon

A keyword can use one or more parameter separated by comma

KEYWORD= parameter1, parameter2, parameter3;

Example:

MSG=SYS-INP;FMOD=1;TYPE=RING

MSG=SYS-INP;FMOD=1;TYPE=RING;DIAL=DTMF,A12345678,B11111111

MSG=SYS-INP;FMOD=7;TYPE=RING-EMERG;DIAL=DTMF,A44445678,B22222222

MSG=SYS-INP;FMOD=1;TYPE=TXBUSY;BUSY=1 (Info frame No response from master)

MSG=SYS-INP;FMOD=1;TYPE=TXBUSY;BUSY=0 (Info frame No response from master)

MSG=SYS-INP;FMOD=2;TYPE=CALL;DIAL=CCIR,12345;RSSI=10

MSG=SYS-INP;FMOD=3;TYPE=CALL;DIAL=DTMF,A12345678,B11111111

MSG=SYS-INP;FMOD=8;TYPE=CALL;DIAL=CCIR,12345;RSSI=10

MSG=SYS-INP;FMOD=2;TYPE=MPTTEXT;DIAL=MPT,030129;DATA=Hello world

MSG=SYS-INP;FMOD=2;TYPE=TXCOMPLETE;DIAL=MPT,030129 (IHM text only)

MSG=SYS-INP;FMOD=1;TYPE=DISCONNECT

MSG=SYS-INP;FMOD=1;TYPE=KEY,1

MSG=SYS-INP;FMOD=1;TYPE=KEY,0

MSG=SYS-INP;FMOD=1;TYPE=SQUELCH,1

MSG=SYS-INP;FMOD=1;TYPE=SQUELCH,0

MSG=SYS-INP;FMOD=1;TYPE=KEYSTATUS,1

MSG=SYS-INP;FMOD=1;TYPE=KEYSTATUS,0

MSG=SYS-INP;FMOD=1;TYPE=TXFINISH;TX=CCIR

MSG=SYS-INP;FMOD=1;TYPE=REPLY;TONE=CCIR,7

MSG=SYS-INP;FMOD=1;TYPE=ERROR;ERR=3,1

MSG=SYS-INP;FMOD=1;TYPE=ERROR;ERR=3,0

MSG=SYS-INP;TYPE=OPTO;INP=2,1

MSG=SYS-INP;TYPE=OPTO;INP=2,0

MSG=SYS-INP;FMOD=27;RSSI=0;TYPE=COM53,”ACK=SPE,1234-5678”

MSG=SYS-INP;FMOD=27; RSSI=0;TYPE=COM53,”CAL=MPT,112211221122”

MSG=SYS-INP;FMOD=27;RSSI=0;TYPE=COM53,”CAL=CCI,12345”

MSG=SYS-INP;FMOD=27; RSSI=10; TYPE=COM53,”INP=ABCDefghS;RSSI=10”

Start cleaning up emergency receiver module 16

MSG=SYS-INP;FMOD=16;TYPE=DISCONNECTEMERGENCY

## SYS-EMERGENCY  command: (Winser -> App-server)

Emergency receiver HM807/2 or HM807/3

MSG=	SYS-EMERGENCY

TYPE=		EMERGRX

DIALTYPE:	[DTMF | FSK | CONFIG]

FMOD=	[Module]

DATA= 	[pair of hex values: 11 = $11, 22=$22, 01=$01]

MSG=SYS-EMERGENCY; TYPE=EMERGRX; FMOD=27; DIALTYPE=DTMF; DATA=112211221122

MSG=SYS- EMERGENCY; TYPE=EMERGRX; FMOD=27; DIALTYPE=FSK; DATA=112211221122

MSG=SYS- EMERGENCY; TYPE=EMERGRX; FMOD=27; DIALTYPE=CONFIG; DATA=112211221122

## SYS-EMERGENCY RINGING command: (Winser -> App-server)

Emergency receiver HM807/2 or HM807/3

MSG=	SYS-EMERGENCY

TYPE=		RING-EMERG	[Emergency ringing from module]

FMOD=	[Module]

DIAL=		[Digittype, Digits]

Digittype: DTMF

Digits:       0123456789ABCDEF*#

ie  [DIAL=DTMF,A12345678,B11111111]

MSG=SYS-EMERGENCY; TYPE=RING-EMERG; FMOD=7; DIAL=DTMF,A44445678,B22222222

### Com53 input  commands

Com53 has 8 input and a squelch (S)

Capital letters indicates active input. Small letters indicates inactive input

INP= A, B, C, D, e, f, g, h , S

RSSI= values between 0 and 15

TXE= TX done on COM53 unit [CCI, ZVE, DTM, SPE, POC, MPT]

MSG=SYS-INP;FMOD=27;TYPE=COM53,”INP=ABCDefghS;RSSI=10”

MSG=SYS-INP;FMOD=27;TYPE=COM53,”INP=aBCDefghs;RSSI=0”

MSG=SYS-INP;FMOD=27;TYPE=COM53,”TXE=CCI”

### Com53 input Call commands

CAL= dial-type[CCI, ZVE, DTM, SPE, POC, MPT], dial number[0..9];Optional commands

CCI: CCIR tone system

ZVE: ZWEI tone system

DTM: DTMF tone system

POC: POCSAG signalling (1200 or 2400 baud)

MPT: MPT signalling  (1200 baud)

SPE: SPEEDA signalling

MSG=SYS-INP;FMOD=27;TYPE=COM53,”CAL=CCI,12345”

MSG=SYS-INP;FMOD=27;TYPE=COM53,”CAL=ZVE,12345”

MSG=SYS-INP;FMOD=27;TYPE=COM53,”CAL=DTM,12345”

MSG=SYS-INP;FMOD=27;TYPE=COM53,”CAL=POC,12345;TXT=”Hello world””

MSG=SYS-INP;FMOD=27;TYPE=COM53,”CAL=MPT,112211221122”

## Tetra Call

Tetra calls uses MSG=SYS-CON;TYPE=HOOK (18.2) for calling a radio in speech mode.

All other commands uses MSG=SYS-OUT (18.4) and MSG=SYS-INP (18.5).

They are all part of SYSCMD and SYSCMD response ( not shown in the examples).

### Incoming speech call from 3317

MSG=SYS-INP;FMOD=1;TYPE=CALL;DIAL=TETRA,3316-3317

Alerting to 3317.

MSG=SYS-OUT;TMOD=1;TYPE=TETRA-ALERT;DIAL=TETRA,3317-3316

Off hook to 3317.

MSG=SYS-OUT;TMOD=1;TYPE=TETRA-HOOKOFF;DIAL=TETRA,3317-3316

On hook from operator.

MSG=SYS-OUT;TMOD=1;TYPE=TETRA-HOOKON;DIAL=TETRA,3317-3316

On hook from 3317

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=HOOKON

### Outgoing speech call to 3317

MSG=SYS-CON;TYPE=HOOK;TMOD=1;DIAL=TETRA,3317-0001

Alerting while calling 3317.

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=ALERT

Off hook from 3317:

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=HOOKOFF

On hook from operator:

MSG=SYS-CON;TMOD=1;TYPE=TETRA-HOOKON;DIAL=TETRA,3317-0001

On hook from 3317

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=HOOKON

### Outgoing text call to 3317

MSG=SYS-OUT;TYPE=TETRA-DATA;TMOD=1;DIAL=TETRA,3317-0001;DATA=Hello World

Text Accept from 3317:

MSG=SYS-INP;FMOD=1;DIAL=TETRA,3316-3317;TYPE=TETRA-REPLY;STATUS=ACCEPT

Text Reject from 3317:

MSG=SYS-INP;FMOD=1;DIAL=TETRA,3316-3317;TYPE=TETRA-REPLY;STATUS=REJECT; SUBSTATUS=Reject text

### Incoming text call from 3317

Tetra SDS call with text (hello). First char in data = 01 hex Data[2 ..n] text displayed

MSG=SYS-INP;FMOD=1;DATAREF=1;TYPE=TETRA-DATA;DIAL=TETRA,3316-3317; DATA=<0x01>Hello World

Text Accept to 3317:

MSG=SYS-OUT;TMOD=1;DATAREF=1;TYPE=TETRA-ACCEPT;DIAL=TETRA,3317-3316

Text Reject to 3317:

MSG=SYS-OUT;TMOD=1;DATAREF=1;TYPE=TETRA-REJECT;DIAL=TETRA,3317-3316

### Incoming status call as text  from 3317

Tetra SDS call with Ihm status 12 as text . First char in data = 02 hex and Data[2 ..n] = status number

MSG=SYS-INP;FMOD=1;TYPE=TETRA-DATA;DIAL=TETRA,3316-3317;

DATAREF=4; DATA=[0x02]12

Accepting SDS call

MSG=SYS-OUT;TMOD=1;TYPE=TETRA-ACCEPT;DIAL=TETRA, 3317-3316; DATAREF=4

Reject SDS call

MSG=SYS-OUT;TMOD=1;TYPE=TETRA-REJECT;DIAL=TETRA, 3317-3316; DATAREF=4

### Group setup to 3316 (local tetra connected to VIU unit)

MSG=SYS-CON;TYPE=TETRA-GROUP;TMOD=1;DIAL=TETRA,8000003-3316

Accept from 3316:

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=ACCEPT;

DIAL=TETRA,8000003-3316

Reject from 3316:

MSG=SYS-INP;FMOD=1;TYPE=TETRA-REPLY;STATUS=REJECT;

DIAL=TETRA,8000003-3316

### Get Immediate GPS Request from 331)

MSG=SYS-OUT;TMOD=1;TYPE=TLREQ;DIAL=TETRA,3317-3316;TRC=?LOC

Answer from 3317

MSG=SYS-INP;FMOD=1;TYPE=GPSI;DIAL=TETRA,3316-3317;RID=3316;DATAREF=4 GPS=1_N55.44.4,8_E12.28.38,3_29.05.2005_09:31:25_000km/h_0deg

### Setup Triggered GPS on 3317

MSG=SYS-OUT;TMOD=1;TYPE=TLREQ;DIAL=TETRA,3317-3316;TRC=?TRC_1_5

Answer from 3317

MSG=SYS-INP;FMOD=1;TYPE=GPST;DIAL=TETRA,3316-3317;RID=3316; GPS=1_N55.44.4,8_E12.28.38,3_29.05.2005_09:31:25_000km/h_0deg

### Unsolicited GPS information from 3317

MSG=SYS-INP;FMOD=1;TYPE=GPSU;DIAL=TETRA,3316-3317;RID=47;

GPS=1_N55.44.4,8_E12.28.38,3_29.05.2005_09:31:25_000km/h_0deg

### Tetra BaseServiceIndication

Tetra BaseServiceIndication: 0 = In Service, 1 = No Registration, 2 = No Service

MSG=SYS-INP;FMOD=1;TYPE=TETRA-SERVICE;INDICATION=0

## SYS CMD Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Error Text | Char | 80 | Spaces |  | Text |
| 4 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

- Message

MSG=Command string from SYSCMD.

The string can bee modified showing XCH=2 and the selected TMOD=2 for first available module.

# SYS ICCS

## SYS ICCS

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Message | Char | 512 | Spaces |  | Commatext |

- ID.

Always zero

- MODE

Always zero.

- API Response call from ICCS to Client Application:

ICCS-RSP=commatext

- API Function call from Client Application to ICCS:

ICCS-CMD=commatext

API Response example: ICCS to Client Application

ICCS-RSP=McaInboundRadioStatus,MCA_DATA_RECEIVED,,,2,Channel2,123,Petersen,4,,,,,

API Function example: Client Application to ICCS

ICCS-CMD=McaBeginPrivateCall,,,,2,Channel2,123,Petersen,,1,Opr0001,,,

## ICCS-CMD  /  ICCS-RSP commatext format

ICCS-CMD / ICCS-RSP =commatext

APIcmd	= 0	//command: McaInBoundStatus / McaInboundPrivateCallStatus / etc.

APIcmdStat	= 1	//Status Field Definition

APIcmdType	= 2	//Type Field Definition

APIcmdMode	= 3	//Mode Field Definition

APIChId	= 4	//ChannelId

APIChName	= 5	//ChannelName

APIUnitId	= 6	//RadioId

APIUnitName	= 7	//RadioName / Alias

APIUnitStat	= 8	//RadioStatus

APICliId	= 9	//ClientId

APICliName	= 10	//ClientName

APICliNo	= 11	//ClientNumber

APIClType	= 12	//ClientType

APIParam1	= 13	//Parameter 1

APIParam2	= 14	//Parameter 2

APIInit        	= ',,,,,,,,,,,,,,';

## Registration functions/responses

API Function:	McdiRegisterClientEx

API Function:	McdiDeRegisterClient

API Response: 	McdiClientRegistrationStatus

## API Function: McdiRegisterClientEx

Register the client with the CDI.

ICCS-CMD=commatext:

[APIcmd]	= McdiRegisterClientEx

[APIcmdStat]	= Authentication UserName

[APIcmdType]	= Authentication Password

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number   [1..8]

If the API Function call fails, API Response

McdiClientRegisterStatus - MESSAGE_REJECTED is returned.

## API Function: McdiDeRegisterClient

De-register the client from the CDI.

ICCS-CMD=commatext:

[APIcmd]	= McdiDeRegisterClient

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McdiClientRegisterStatus - MESSAGE_REJECTED is returned.

## API Response: McdiClientRegistrationStatus

A client has registered or de-registered with the CDI.

ICCS-RSP=commatext:

[APIcmd]	= McdiClientRegistrationStatus

[APIcmdStat]	= MCDI_REGISTRATION_SUCCESSFUL

MCDI_INVALID_CLIENT_TYPE

MCDI_DIFFERENT_CLIENT_TYPE_EXISTING

MCDI_REGISTRATION_INTERNAL_FAIL

MCDI_CLIENT_TYPE_TOO_LONG

MCDI_INVALID_REGISTRATION_MODE

MESSAGE_REJECTED

[APIcmdMode]	= MCDI_REGISTERED

MCDI_DEREGISTERED

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## AssignResource functions/responses

API Function:	McaAssignResourceEx

API Function:	McaDeassignResource

API Response:	McaAssignmentStatus

API Response: 	McaAssignResourceError

API Response:	McaAssignResourceWarning

API Response:	McaDeassignResourceError

API Response: 	McaDeassignResourceWarning

## API Function: McaAssignResourceEx

Assign resource to Client.

ICCS-CMD=commatext:

[APIcmd]	= McaAssignResourceEx

[APIChName]	= Empty. Auto assign all PrivateCall and TalkGroup resources to client.

<> Empty. Resource DatabaseName to assign.

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	<> Empty. URid = The unified resource ID to assign to the Client.

If the API Function call fails, API Response

McaAssigmentResourceError - MESSAGE_REJECTED is returned.

## API Function: McaDeassignResource

Deassign resource from a Client.

ICCS-CMD=commatext:

[APIcmd]	= McaDeassignResource

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	<> Empty. URid = The unified resource ID to deassign.

If the API Function call fails, API Response

McaDeassignError - MESSAGE_REJECTED is returned.

## API Response: McaAssignmentStatus

Report the status of a resource assignment to a Client.

ICCS-RSP=commatext:

[APIcmd]	= McaAssignmentStatus

[APIcmdStat]	= MCA_RESOURCE_ASSIGNED

MCA_RESOURCE_DEASSIGNED

MCA_ALL_RESOURCES_DEASSIGNED

[APIcmdType]	= MCA_STATUS_UPDATE

MCA_STATUS_REFRESH

[APIcmdMode] = Empty

MCDB_PRIVATE_CALL

MCDB_SINGLE_SELECT

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	<> Empty. URid = The unified resource ID assigned to the Client.

Note!

The APIChId	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID) is only

operational after receiving.

[APIcmd]	= McaResourceStatus

[APIcmdStat]	= MCA_RESOURCE_AVAILABLE

[APIChId]	= Correct Channel ID

## API Response: McaAssignResourceError

An error has occurred while trying to assign a resource to a Client.

ICCS-RSP=commatext:

[APIcmd]	= McaAssignResourceError

[APIcmdStat]	= MCA_INVALID_URID

MCA_INVALID_LC_ID

MCA_NO_AVAILABLE_LC_ID

MCA_INTERNAL_DB_ERROR

MCA_NOT_DEASSIGNED_TRANSMITTING

MCA_NOT_DEASSIGNED_IN_PATCH_GROUP

MCA_NOT_DEASSIGNED_EMERGENCY_ACTIVITY

MCA_NOT_DEASSIGNED_RSC_OFF_HOOK

MCA_ASSIGNMENT_IN_PROGRESS

MCA_RSC_ALREADY_ASSIGNED

MCA_LCID_ALREADY_ASSIGNED

MCA_OP_DISABLED

MCA_INVALID_SELECT_SPEAKER_ID

MCA_INVALID_UNSELECT_SPEAKER_ID

MCA_INVALID_HEADSET_SELECT

MCA_INVALID_VOLUME_LEVEL

MCA_NOT_ASSIGNED_TNNR_TX_FAIL

MCA_INVALID_CRITICAL_RSC_SETTING

MCA_PLATFORM_MISMATCH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaAssignResourceWarning

A warning has occurred while trying to assign a resource to a Client.

ICCS-RSP=commatext:

[APIcmd]	= McaAssignResourceWarning

[APIcmdStat]	= MCA_RSC_ASGN_NOT_CRITICAL

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaDeassignResourceError

An error has occurred while trying to assign a resource from a client.

ICCS-RSP=commatext:

[APIcmd]	= McaDeassignResourceError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_PRIORITY

MCA_OP_DISABLED

MCA_RSC_IN_PATCH_GROUP

MCA_RSC_HAS_EMERGENCY

MCA_RSC_OFF_HOOK

MCA_RSC_TRANSMITTING

MCA_PLATFORM_MISMATCH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaDeassignResourceWarning

An warning has occurred while trying to assign a resource from a client.

ICCS-RSP=commatext:

[APIcmd]	= McaDeassignResourceWarning

[APIcmdStat]	= MCA_MAX_LC_ID_CHANGED_WRN

MCA_RESOURCE_DELETED_WRN

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## PrivateCall functions/responses

API Response:	McaPrivateCallStatus

API Function: 	McaBeginPrivateCall

API Function:	McaAnswerPrivateCall

API Function: 	McaEndPrivateCall

API Function: 	McaRejectPrivateCall

API Response: 	McaBeginPrivateCallError

API Response: 	McaAnswerPrivateCallError

API Response: 	McaRejectPrivateCallError

API Response: 	McaEndPrivateCallError

## API Response: McaPrivateCallStatus

Report the status of a private call request.

ICCS-RSP=commatext:

[APIcmd]	= McaPrivateCallStatus

[APIcmdStat]	= MCA_ATTEMPTING_TO_SEND

MCA_TARGET_RINGING

MCA_BEGUN

MCA_ENDED

MCA_REJECTED

[APIcmdType]	= MCA_STATUS_UPDATE

MCA_STATUS_REFRESH

[APIcmdMode]	= MCA_SIMPLEX

MCA_FULL_DUPLEX

MCA_UNKNOWN

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Function: McaBeginPrivateCall

Initiate a private call to the specified target unit from an operator position.

ICCS-CMD=commatext:

[APIcmd]	= McaBeginPrivateCall

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McaBeginPrivateCallError - MESSAGE_REJECTED is returned.

## API Function: McaAnswerPrivateCall

Answer an inbound private call request sent by a radio unit.

ICCS-CMD=commatext:

[APIcmd]	= McaAnswerPrivateCall

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McaAnswerPrivateCallError - MESSAGE_REJECTED is returned.

## API Function: McaEndPrivateCall

End the current private call on a specified resource.

ICCS-CMD=commatext:

[APIcmd]	= McaEndPrivateCall

[APIChId]	= ChannelId

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McaEndPrivateCallError - MESSAGE_REJECTED is returned.

## API Function: McaRejectPrivateCall

Reject an inbound private call request sent by a radio unit.

ICCS-CMD=commatext:

[APIcmd]	= McaRejectPrivateCall

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McaRejectPrivateCallError - MESSAGE_REJECTED is returned.

## API Response: McaBeginPrivateCallError

Report the failure of the McaBeginPrivateCall.

ICCS-RSP=commatext:

[APIcmd]	= McaBeginPrivateCallError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_UNIT_ID

MCA_DATA_PATH_NOT_AVAILABLE

MCA_NO_ACK_RECEIVED

MCA_RESOURCE_NOT_AVAILABLE

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_APPLICATION_CONFLICT

MCA_NO_ANSWER

MCA_PLATFORM_MISMATCH

MESSAGE_REJECTED

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaAnswerPrivateCallError

Report the failure of the McaAnswerPrivateCall function.

ICCS-RSP=commatext:

[APIcmd]	= McaAnswerPrivateCallError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_UNIT_ID

MCA_DATA_PATH_NOT_AVAILABLE

MCA_RESOURCE_NOT_AVAILABLE

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_NOT_IN_PROGRESS

MCA_PLATFORM_MISMATCH

MESSAGE_REJECTED

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaRejectPrivateCallError

Report the failure of the McaRejectPrivateCall function.

ICCS-RSP=commatext:

[APIcmd]	= McaRejectPrivateCallError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_UNIT_ID

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_PLATFORM_MISMATCH

MCA_INVALID_RETRY_ID

MCA_RESOURCE_NOT_AVAILABLE

MCA_RSC_TRANSMITTING

MCA_NOT_IN_PROGRESS

MCA_DATA_PATH_NOT_AVAILABLE

MESSAGE_REJECTED

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaEndPrivateCallError

Report the failure of the McaEndPrivateCall function.

ICCS-RSP=commatext:

[APIcmd]	= McaEndPrivateCallError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_RESOURCE_NOT_AVAILABLE

MCA_DATA_PATH_NOT_AVAILABLE

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_RSC_TRANSMITTING

MCA_APPLICATION_CONFLICT

MCA_PLATFORM_MISMATCH

MESSAGE_REJECTED

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## EmergencyCall functions/responses

API Response: 	McaEmergencyCallStatus

API Response: 	McaEmergencyAlarmStatus

API Function:	McaAcknowledgeEmergency

API Response:	McaAcknowledgeEmergencyError

API Function: 	McaEndEmergency

API Response: 	McaEndEmergencyError

API Response: 	McaBeginConsoleEmergencyCallError

## API Response: McaEmergencyCallStatus

Reports the status of an emergency call.

ICCS-RSP=commatext:

[APIcmd]	= McaEmergencyCallStatus

[APIcmdStat]	= MCA_EMERG_CALL_STATE

MCA_EMERG_ENDED

MCA_UNACKNOWLEDGED_EMERG_CALL_REFRESH

MCA_ACKNOWLEDGED_EMERG_CALL_REFRESH

MCA_EMERG_CALL_ENDED_REFRESH

MCA_PATCHED_EMERG_CALL_STATE

MCA_PATCHED_EMERG_CALL_REFRESH

[APIcmdType]	= MCA_CONSOLE_INITIATED

MCA_RADIO_INITIATED

MCA_EXT_SUBSCRIBER_INITIATED

MCA_INT_SUBSCRIBER_INITIATED

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaEmergencyAlarmStatus

Report the status of an emergency.

ICCS-RSP=commatext:

[APIcmd]	= McaEmergencyAlarmStatus

[APIcmdStat]	= MCA_RADIO_EMERG_ALARM_RECEIVED

MCA_EMERG_ACKNOWLEDGED

MCA_EMERG_ALARM_ENDED

MCA_ACKNOWLEDGED_EMERG_ALARM_ REFRESH

MCA_UNACKNOWLEDGED_EMERG_ALARM_ REFRESH

MCA_EMERG_ALARM_ENDED_REFRESH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

By MCA_EMERG_ACKNOWLEDGED &

MCA_ACKNOWLEDGED_EMERG_ALARM_ REFRESH:

[APIParam1]	= ClientId of acknowledging Operator

[APIParam2]	= Operator Resource (Opr0001..Opr000x) of acknowledging Operator

## API Function: McaAcknowledgeEmergency

Indicates that a console operator has acknowledged the emergency alarm or call for a specified radio on a specified resource and has taken responsibility for handling the emergency.

ICCS-CMD=commatext:

[APIcmd]	= McaAcknowledgeEmergency

[APIChId]	= ChannelId

[APIUnitId]	= Unit number

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McaAcknowledgeEmergencyError - MESSAGE_REJECTED is returned.

## API Response: McaAcknowledgeEmergencyError

An error occurred while a console operator attempted to acknowledge an emergency alarm or call

ICCS-RSP=commatext:

[APIcmd]	= McaAcknowledgeEmergencyError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_UNIT_ID

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_RSC_DEASSIGNED

MCA_RESOURCE_NOT_AVAILABLE

MCA_PLATFORM_MISMATCH

MESSAGE_REJECTED

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Function: McaEndEmergency

Ends emergency calls and emergency alarms on a specified resource.

ICCS-CMD=commatext:

[APIcmd]	= McaEndEmergency

[APIChId]	= ChannelId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

If the API Function call fails, API Response

McdiClientRegisterStatus - MESSAGE_REJECTED is returned.

## API Response: McaEndEmergencyError

An error has occurred when trying to end an emergency call or alarm.

ICCS-RSP=commatext:

[APIcmd]	= McaEndEmergencyError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_RESOURCE_NOT_AVAILABLE

MCA_DATA_PATH_NOT_AVAILABLE

MCA_EMAC_RESTRICTED_OP

MCA_PLATFORM_MISMATCH

MESSAGE_REJECTED

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaBeginConsoleEmergencyCallError

An error has occurred when trying to setup a console initiated emergency call.

ICCS-RSP=commatext:

[APIcmd]	= McaBeginConsoleEmergencyCallError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_RSC_DEASSIGNED

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_RESOURCE_NOT_AVAILABLE

MCA_DATA_PATH_NOT_AVAILABLE

MCA_APPLICATION_CONFLICT

MCA_PLATFORM_MISMATCH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## Select/DeselectResource (talk group) functions/responses

API Function: 	McaSelectResource

API Response: 	McaSelectResourceError

API Function: 	McaDeSelectResource

API Response: 	McaDeSelectResourceError

API Response: 	McaResourceSelectStatus

API Response: 	McaCriticalResourceStatus

## API Function: McaSelectResource

Attempt to select a single resource (talk group).

ICCS-CMD=commatext:

[APIcmd]	= McaSelectResource

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaSelectResourceError

An error has occurred while trying to Single Select a resource (talk group).

ICCS-RSP=commatext:

[APIcmd]	= McaSelectResourceError

[APIcmdStat]	= MCA_CANNOT_DESELECT

MCA_INVALID_LC_ID

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_NOT_IN_SINGLE_SELECT_MODE

MCA_RSC_DEASSIGNED

MCA_RSC_TRANSMITTING

MCA_PLATFORM_MISMATCH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Function: McaDeSelectResource

Attempt to deselect a single resource (talk group).

ICCS-CMD=commatext:

[APIcmd]	= McaDeSelectResource

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaDeSelectResourceError

An error has occurred while trying to deselect a resource (talk group).

ICCS-RSP=commatext:

[APIcmd]	= McaDeSelectResourceError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_NOT_ALLOWED_FOR_THIS_RSC

MCA_NOT_IN_SINGLE_SELECT_MODE

MCA_RSC_DEASSIGNED

MCA_RSC_TRANSMITTING

MCA_PLATFORM_MISMATCH

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaResourceSelectStatus

Report the select status of the specified resource.

ICCS-RSP=commatext:

[APIcmd]	= McaResourceSelectStatus

[APIcmdStat]	= MCA_RSC_SELECTED

MCA_RSC_DESELECTED

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaResourceStatus

Report a change in resource’s availability.

ICCS-RSP=commatext:

[APIcmd]	= McaResourceStatus

[APIcmdStat]	= MCA_RESOURCE_NOT_OPERATIONAL

MCA_RESOURCE_ASSIGNED

MCA_RESOURCE_DEASSIGNED

MCA_ALL_RESOURCES_DEASSIGNED

MCA_RESOURCE_NOT_AVAILABLE

MCA_RESOURCE_AVAILABLE

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaCriticalResourceStatus

Report the critical status of a given resource.

ICCS-RSP=commatext:

[APIcmd]	= McaCriticalResourceStatus

[APIcmdStat]	= MCA_NON_CRITICAL_RESOURCE

MCA_CRITICAL_RESOURCE

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## Inbound Call responses

API Response: 	McaInboundRadioStatus

API Response: 	McaInboundPrivateCallStatus

API Response: 	McaInboundCallStatus

API Response: 	McaInboundPttIdStatus

## API Response: McaInboundRadioStatus

Report the reception of an inbound radio status.

ICCS-RSP=commatext:

[APIcmd]	= McaInboundRadioStatus

[APIcmdStat]   =  MCA_DATA_RECEIVED

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APIUnitStat]	= RadioStatus

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001…Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaInboundPrivateCallStatus

Report the status of an inbound private call request.

ICCS-RSP=commatext:

[APIcmd]	= McaInboundPrivateCallStatus

[APIcmdStat]	= MCA_INBOUND_RADIO_PVT_CALL

[APIcmdType]	= MCA_STATUS_UPDATE

MCA_STATUS_REFRESH

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APIUnitId]	= RadioId

[APIUnitName]	= RadioName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	= HeadNumber			(Only for Dimetra 6.2 SSR and newer)

[APIParam2]	= HeadNumberAlias		(Only for Dimetra 6.2 SSR and newer)

## API Response: McaInboundCallStatus

The specified resource has detected an inbound call.

ICCS-RSP=commatext:

[APIcmd]	= McaInboundCallStatus

[APIcmdStat]	= MCA_BEGUN

MCA_BEGUN_WITHOUT_AUDIO

MCA_ENDED

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIcmdMode]	= MCA_RSC_SELECTED_HERE

MCA_RSC_NOT_SELECTED_HERE

MCA_NULL_RSC_SELECT_STATUS

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaInboundPttIdStatus

Report the reception of an inbound PTT ID.

ICCS-RSP=commatext:

[APIcmd]	= McaInboundPttIdStatus

[APIcmdStat]	= MCA_RADIO_INITIATED_PTT

MCA_CONSOLE_INITIATED_PTT

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIUnitId]	= Unit number

[APIUnitName]	= Unit Name

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## Volume Control  functions/responses

API Function: 	McaChangeVolume

API Response: 	McaResourceVolumeStatus

API Response: 	McaChangeVolumeError

## API Function: McaChangeVolume

Attempt to change the volume level of a specified resource.

ICCS-CMD=commatext:

[APIcmd]	= McaChangeVolume

[APIcmdMode]	= VolumeLevel 1-8 (1 being the quietest and 8 being the loudest)

[APIChId]	= ChannelId

[APIChName]	= ChannelName

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaResourceVolumeStatus

Report the current volume level of the specified resource.

ICCS-RSP=commatext:

[APIcmd]	= McaResourceVolumeStatus

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIcmdMode]	= VolumeLevel 1-8 (1 being the quietest and 8 being the loudest)

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaChangeVolumeError

An error has occurred while trying to change the volume on a resource.

ICCS-RSP=commatext:

[APIcmd]	= McaChangeVolumeError

[APIcmdStat]	= MCA_INVALID_LC_ID

MCA_INVALID_VOLUME_LEVEL

MCA_PLATFORM_MISMATCH

MCA_RSC_DEASSIGNED

[APIcmdMode]	= VolumeLevel 1-8 (1 being the quietest and 8 being the loudest)

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## Transmit  functions/responses

API Function: 	McaBeginInstantTransmit

API Response:	McaBeginInstantTransmitError

API Function: 	McaEndInstantTransmit

API Response: 	McaEndInstantTransmitError

API Response: 	McaResourceTransmitStatus

API Response:  McaResourceTransmitStatus

API Response: 	McaGeneralTransmitStatus

## API Function: McaBeginInstantTransmit

Begin an instant transmit on a specific resource.

ICCS-CMD=commatext:

[APIcmd]	= McaBeginInstantTransmit

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaBeginInstantTransmitError

An error has occurred when trying to begin an instant transmit.

ICCS-RSP=commatext:

[APIcmd]	= McaBeginInstantTransmitError

[APIcmdStat]	= MCA_XXXXXXXXX

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Function: McaEndInstantTransmit

End an instant transmit on a specific resource.

ICCS-CMD=commatext:

[APIcmd]	= McaEndInstantTransmit

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaEndInstantTransmitError

An error has occurred when trying to end an instant transmit.

ICCS-RSP=commatext:

[APIcmd]	= McaEndInstantTransmitError

[APIcmdStat]	= MCA_XXXXXXXXX

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APIChName]	= ChannelName (assigned resource DatabaseName)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaResourceTransmitStatus

Resource transmit status for a specific resource.

ICCS-RSP=commatext:

[APIcmd]	= McaResourceTransmitStatus

[APIcmdStat]	= MCA_TRANSMIT_BEGUN

MCA_TRANSMIT_IDLE

MCA_TRANSMIT_PENDING

MCA_ALL_RESOURCES_DEASSIGNED

MCA_RESOURCE_NOT_AVAILABLE

MCA_RESOURCE_AVAILABLE

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APIChId]	= ChannelId 	 (assigned resource LC_ID – Logical Channel ID)

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## API Response: McaGeneralTransmitStatus

Report the status of the general transmit function.

ICCS-RSP= commatext:

[APIcmd]	= McaGeneralTransmitStatus

[APIcmdStat]	= MCA_BEGUN

MCA_ENDED

MCA_PAGING_TALK_IDLE

MCA_PAGING_TALK_WAITING

MCA_PAGING_TALK_PERMITTED

MCA_PAGING_TALK_BEGUN

[APIcmdType]	= MCA_STATUS_REFRESH

MCA_STATUS_UPDATE

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

## McdbGetOpId  functions/responses

API Function: 	McdbGetOpId

API Response:	McdbGetOpIdResponse

API Response:	McdbGetOpIdError

## API Function: McdbGetOpId

Get the Unified Resource Identifier (URID) for the local operator position.

ICCS-CMD=commatext:

[APIcmd]	= McdbGetOpId

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number   [1..8]

If the API Function call fails, API Response

McdbGetOpIdError - MESSAGE_REJECTED is returned.

## API Response: McdbGetOpIdResponse

McdbGetOpIdResponse for the Unified Resource Identifier (URID) for the local operator position.

ICCS-RSP=commatext:

[APIcmd]	= McdbGetOpIdResponse

[APIcmdStat]	= MCDB_NO_ERROR

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	= Unified Resource Identifier (URID)

## API Response: McdbGetOpIdError

McdbGetOpIdError for the Unified Resource Identifier (URID) for the local operator position.

ICCS-RSP=commatext:

[APIcmd]	= McdbGetOpIdError

[APIcmdStat]	= MCDB_INVALID_DB_HANDLE

MCDB_COMMUNICATION_FAILURE

MCDB_RETRIEVAL_UNSUCCESSFULL

MCDB_RECORD_NOT_FOUND

MCDB_INVALID_PARAMETER

MESSAGE_REJECTED

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

[APIParam1]	= Empty (No URID)

## API Response: OperProcessStatus

OperProcessStatus running not running

ICCS-RSP=commatext:

[APIcmd]	= OperProcessStatus

[APIcmdStat]	= IHM_NOT_RUNNING

IHM_RUNNING

[APICliId]	= ClientId

[APICliName]	= Operator Resource (Opr0001..Opr000x)

[APICliNo]	= Operator Client number (1..x)

SYSICCS Response.

| Field No. | Field Name | Data type | Length in bytes | Initialize to | Allowed values | Comments |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | ID. | Unsigned Long | 4 | 0 | 0 | Identification number generated by the master control |
| 2 | Mode | Unsigned Short | 2 | 0 |  | Not used yet |
| 3 | Error Text | Char | 80 | Spaces |  | Text |
| 4 | Message | Char | 512 | Spaces |  | Comma separated text |

- ID.

Always zero

- MODE

Always zero.

- ERROR TEXT.

Any text describing the error, if Result Code in header is different from zero.

- Message

MSG=Command string from SYSICCS.

The string can bee modified

# Emergency receiver HM674/8

CALL_EMERG – DTMF digit format support up to 40 digits:

Normal call without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Normal call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Normal call without prefix and phone number: CZ#XX&AAAAAAAA&VVVVVVVV#YYYYY#

Normal call with prefixes and phone number:

CZ#XX&AAAAAAAA*PP*VVVVVVVV#YYYYYY#

Z:	“0” = No speech

“1” = speech.

XX:	TR_TYPE.

TR_TYPE = “01”	-	CARRES

TR_TYPE = “02”	-	FS90

TR_TYPE = “03”	-	FC2000

TR_TYPE = “04”	-	TTU04/SAS10 (L400)

TR_TYPE = “05”	-	CAMILLO

TR_TYPE = “06”	-	TRYGGO

TR_TYPE = “07”	-	Solo

TR_TYPE = “08”	-	Portal

TR_TYPE = “09”	-	Lifeline

TR_TYPE = “10”	-	Piper

TR_TYPE = “11”	-	SAS10 ELECTROLUX

TR_TYPE = “12”	-	REHAB40

TR_TYPE = “15”	-	SCANCOM fast 8 bit parallel

TR_TYPE = “16”	-	TSA3100

TR_TYPE = “17”	-	TSA3100

TR_TYPE = “18”	-	MONITOR PIPER – SOLO (old)

TR_TYPE = “19”	-	MONITOR PIPER – PORTAL

TR_TYPE = “20”	-	MONITOR PIPER – LIFELINE, SOLO (2,3)

TR_TYPE = “21”	-	MONITOR PIPER – SCHEME Group system

TR_TYPE = “22”	-	GSM phone

TR_TYPE = “23”	-	Scan Com Slow

TR_TYPE = “24”	-	P-100

TR_TYPE = “25”	-	Silent Knight

TR_TYPE = “26”	-	Scan Com Fast 16 bit parallel

TR_TYPE = “27”	-	Protocol error – using phone number as ID

TR_TYPE = “28”	-	TMA protocol

No prefix:

AAAAAAAA:  Variable phone number

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYY:	Zones - Alarm information - (“00001” for input 1 decimal)

#:		Separator

&:		Phone number Separator

Prefix:

AAAAAAAA:  Variable phone number

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYYY:	Zones - Alarm information - (“000001” for input 1 decimal)

*:		Prefix separator

#:		Separator

&:		Phone number Separator

Command examples.

Emergency RING with or without dial information!

MSG=SYS-INP;FMOD=7;TYPE=RING-EMERG;DIAL=DTMF,A44441234,B22222277

Transmit response

Hook off information to module

MSG=SYS-CON;TMOD=7;TYPE=HOOK

Wait for response. If not suppressed (NoHookResponse=1  - P45453.ini).

Receive emergency call information

MSG=SYS-INP;FMOD=7;TYPE=CALL-EMERG;DIAL=DTMF, C1#01#00005678#00001#

Transmit response

Accept emergency call information

MSG=SYS-OUT;TMOD=7;TYPE= EMERG-ACCEPT,1

Wait for response

You can omit next command. Emergency accept will be reset on disconnect.

MSG=SYS-OUT;TMOD=7; TYPE= EMERG-ACCEPT,0

Wait for response

MSG=SYS-INP;FMOD=8;TYPE=RING-EMERG;DIAL=DTMF,A44442233,B22222288

MSG=SYS-CON;TMOD=8;TYPE=HOOK

MSG=SYS-INP;FMOD=8;TYPE=CALL-EMERG;DIAL=DTMF, C1#01*07*00005678#000001#

MSG=SYS-OUT;TMOD=8;TYPE= EMERG-ACCEPT,1

MSG=SYS-OUT;TMOD=8; TYPE= EMERG-ACCEPT,0

MSG=SYS-INP;FMOD=9;TYPE=RING-EMERG;DIAL=DTMF,A39663131,B22222299

MSG=SYS-CON;TMOD=9;TYPE=HOOK

MSG=SYS-INP;FMOD=9;TYPE=CALL-EMERG;DIAL=DTMF, C1#01&39663131*07*00005678#000001#

MSG=SYS-OUT;TMOD=9;TYPE= EMERG-ACCEPT,1

MSG=SYS-OUT;TMOD=9; TYPE= EMERG-ACCEPT,0

## CALL_EMERG – DTMF digit format GSM Phone Alarm:

Normal call without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Normal call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Normal call without prefix and with A-phone number: CZ#XX&AAAAAAA…A&VVVVVVVV#YYYYY#

Normal call with prefixes and with A-phone number:

CZ#XX&AAAAAAA…A*PP*VVVVVVVV#YYYYYY#

Z:	“0” = No speech

“1” = speech.

XX:	TR_TYPE.

TR_TYPE = “22”	-	GSM phone

No prefix:

AAAAAAA…A:  Variable phone number length 0 to 12 (only with A-phone number)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345” or last 8 digits in A-phone

number)

YYYYY:	Zones - Alarm information - (“00009” = fault no alarm ID)

YYYYY:	Zones - Alarm information - (“00099” GSM call)

#:		Separator

&:		Phone number Separator (only with A-phone number)

Prefix:

AAAAAAA…A:  Variable phone number length 0 to 12 (only with A-phone number)

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345” or last 8 digits in A-phone

number)

YYYYYY:	Zones - Alarm information - (“000009” = fault no Alarm ID)

YYYYYY:	Zones - Alarm information - (“000099” GSM call)

*:		Prefix separator

#:		Separator

&:		Phone number Separator (only with A-phone number)

Example using A-Phone number and no Alarm ID  (“000009” = fault no Alarm ID)

A-Phone number = 12 digits 1234AAAAAAAA
VVVVVVVV = AAAAAAAA

A-Phone number = 8 digits AAAAAAAA
VVVVVVVV = AAAAAAAA

A-Phone number = 4 digits AAAA
0000VVVV   = AAAA

## SCANCOM Alarm

Calls without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Normal call without prefix and phone number: CZ#XX&AAAAAAAA&VVVVVVVV#YYYYY#

Normal call with prefixes and phone number:

CZ#XX&AAAAAAAA*PP*VVVVVVVV#YYYYYY#

Z:	“0 “= No speech		(Speech or no speech have no meaning)

“1” = speech.

XX:	TR_TYPE.

TR_TYPE = “15”	-	SCANCOM

TR_TYPE = “26”	-	Scan Com Fast 16 bit parallel

No prefix

AAAAAAAA:  Variable phone number

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYY:	Alarm using one or more bits – “00129” for bit 7 and bit 0 activated.

#:		 Separator

&:		Phone number Separator

Prefix

AAAAAAAA:  Variable phone number

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYYY:	Alarm using one or more bits – “000129” for bit 7 and bit 0 activated.

(Bit0 -bit7 = alarm zones)  Bit 8 = battery fault

*:		 Prefix separator

#:		 Separator

&:		Phone number Separator

Prefix		16 bit parallel

AAAAAAAA:  Variable phone number

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYYY:	Alarm using one or more bits – “000129” for bit 7 and bit 0 activated.

(Bit0 - bit15 = alarm zones)  Bit 16 = battery fault only with prefix

*:		 Prefix separator

#:		 Separator

&:		Phone number Separator

PS

Only the database knows, if it is a technical or an emergency alarm.

## Lift Alarm

Calls without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Normal call without prefix and phone number: CZ#XX&AAAAAAAA&VVVVVVVV#YYYYY#

Normal call with prefixes and phone number:

CZ#XX&AAAAAAAA*PP*VVVVVVVV#YYYYYY#

Z:	“0” = No speech

“1” = speech.

XX:	TR_TYPE.

TR_TYPE = “16”	-	TSA3100

No prefix

AAAAAAAA:  Variable phone number

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYY:	Alarm using one or more bits – “00129” for bit 7 and bit 0 activated.

00000:		Poll – All bits zero

#:		Separator.

&:		Phone number Separator

Prefix

AAAAAAAA:  Variable phone number

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYYY:	Alarm using one or more bits – “000129” for bit 7 and bit 0 activated.

000:		Poll – All bits zero

*:		Prefix separator.

#:		Separator.

&:		Phone number Separator

PS

Receiving a poll  – Set new time for next poll

Time for reprogramming the next poll

DTMF Format #XXXX#YYYY# to module (use HOOK OFF REQ)

XXXX current time in minutes to 24.00 (midnight)

YYYY next time in minutes from 24.00 (midnight) to next poll

## Beach Alarm

Calls without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Normal call without prefix and phone number: CZ#XX&AAAAAAAA&VVVVVVVV#YYYYY#

Normal call with prefixes and phone number:

CZ#XX&AAAAAAAA*PP*VVVVVVVV#YYYYYY#

Z:	“0” = No speech

“1” = speech.

XX:	TR_TYPE.

TR_TYPE = “17”	-	TSA3100

No prefix

AAAAAAAA:  Variable phone number

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYY:	Alarm using one or more bits – “00003” for bit 1 and bit 0 activated

#:		Separator.

&:		Phone number Separator

Prefix

AAAAAAAA:  Variable phone number

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID, v = variable. (“00012345”)

YYYYYY:	Alarm using one or more bits – “000003” for bit 1 and bit 0 activated

*:		Prefix separator.

#:		Separator.

&:		Phone number Separator

## Protocol error Alarm

Calls without prefix: 	CZ#XX#VVVVVVVV#YYYYY#

Call with prefix: 	CZ#XX*PP*VVVVVVVV#YYYYYY#

Z:	“0” = No speech

XX:	TR_TYPE.

TR_TYPE = “27” - Protocol error – using phone number as ID (if present).

No prefix

VVVVVVVV:	[Null pad] Alarm ID= phone number for unknown alarm,

V = variable. (“00012345”)

YYYYY:	Alarm  (“00001”)

#:		Separator.

Prefix

PP:		Prefix – (“00” – “99”)

VVVVVVVV:	[Null pad] Alarm ID= phone number for unknown alarm,

YYYYYY:	Alarm  (“000001”)

*:		Prefix separator.

#:		Separator.

Special Log Call: DVVVVVVVV#XX#YYY#

VVVVVVVV:	[Null pad] Alarm ID, v = variable

XX:		Call number

YYY:		Zones - Alarm information

#:		Separator.