DIGITAL  HAPPENINGS  #20
(March 2014)
By W0NAC (“Matt”)

I’m happy to report that the new antenna mount seems to be working very well.  I had a machinist enlarge the trailer hitch mounting hole and other parts to 1 ¼” and a local ham friend produced a new spool shaped insulator (photo below) using his 3-D printing machine (these new 3-D printers can do miraculous things!).  I have temporarily assembled the mount (photo below) and on the air reports have been good.

A little later I will be re-assembling the mount using a special epoxy potting compound (excellent insulating qualities) which I hope will prevent road salt, etc. from corroding the metal parts.

Having learned my lesson the hard way, I have also installed a Comet trunk lip mount to use with assorted “Ham Sticks” for backup purposes.  Brief A/B comparison tests show that the 20M Ham Stick puts out almost as strong a signal as my primary antenna.

Incidentally, N0KV put me on to some excellent quick-disconnect hardware made by Breedlove Mounts Inc.  You can locate them using this link: https://breedlovemounts.com/Home_Page.php .  They make a ton of other mounting stuff which is all first class!  I am using their quick disconnects for several assorted Ham Sticks and will be using one on the main mast for my primary antenna.

You can see what is pretty close to my final setup in the photo below:

Even though both antennas seem to work well when they are both mounted at the same time, they do show substantial coupling effects.  For this reason the Ham Sticks will probably remain in the trunk for emergency use only.

How To Find And Work Other Digital Mobiles:

As promised last month, I will try to finish answering the question:  “How in the @!X*#!  do I find and work other digital county hunters?”.

The last two tools I will discuss this month are RSID (Reed Solomon Identification) and Video mode display.  Both of these are well supported by Fldigi software so I will discuss them as implemented in Fldigi.  I’m sure that other digital software programs also support these tools, but time and space limits me to just Fldigi.  As an aside, I am continually being more impressed with Fldigi!  This program somehow achieves the lofty goal of having a rich set of features and settings, but at the same time being simple to use if you just use the default settings.  I highly recommend it to all (and it’s free!). You can download the latest version (3.21.80) here: http://www.w1hkj.com/download.html

Reed Solomon ID:

This is a special transmission (usually added at the beginning) which has a unique code for each mode/sub-mode that your are using.  It was designed by Patrick Lindecker, F6CTE, for the modem program MultiPsk.  It has been adapted to Fldigi and other modem programs.  Fldigi has a separate RSID decoder that operates in parallel with all other modem decoders.

RSID reception and the transmission of RSID codes are toggled ON and OFF by clicking on buttons in the upper right of the Fldigi screen (see photo).

Note that in this picture, both RSID reception and RSID transmission are turned ON as indicated by the small green indicator light in each button.

There are many options available for both receiving and transmitting RSID signals. These are selected in the Configure/ID/RsID menu:

You will need to read the Fldigi manual (Heaven forbid!) to fully understand what each of these settings do, but if you just match the settings shown above things will probably work OK.

The other menu with settings for RSID is under Configure/Notification as follows:

Again, reading the Fldigi manual is recommended, but if you simply make your setup screen look exactly like this one, RSID should work OK.  To be sure, click on the “Test” button and you should see a pop-up notification message similar to this:

A message (or several messages) like this is the end result of monitoring a frequency range where other people’s signals are appearing on your waterfall (If they are transmitting an RSID code).  Note that the message shows the mode/sub-mode they are using and their offset frequency on your waterfall. If you click on the “Go to 1025 Hz” button, Fldigi will automatically change your frequency to match theirs and ALSO change your mode/sub-mode to match their mode/sub-mode!

My initial opinion is that RSID has limited value for county hunters (mobiles) running counties using digital modes or for fixed station county hunters trying to work the mobiles.  I believe this is true because the mobile’s call, mode, and frequency are probably already known, particularly if they have been “spotted”.  Also, nothing is free in this world.  So it is with RSID.  It takes additional time at the beginning of a transmission to transmit the RSID code before any of your message text is sent.  It may be short, but when you are trying to be as fast and efficient as possible, every extra second is very noticeable. Also, right now, most county hunters won’t be set up to receive your RSID code so all they will notice is a funny set of tones at the beginning of your transmissions.

If you are just “trolling” for casual contacts hoping to log new counties or new modes, it looks like RSID could quickly solve the mystery of what mode/sub-mode they are using plus switch you over to their frequency and mode almost instantly.  This could be a real boon!  The only drawback is that not every digital signal you see will be sending an RSID code.  It’s still a bit new for many people.

VIDEO  ID & VIDEO TEXT:

Unlike RSID which just pops up a message, Video ID/Text actually displays brief mode IDs or other short text messages (or both!) at the beginning of your trace on the other person’s waterfall.  Here are some examples:

Video ID Only                                Video Text Only                         Both Video Text & ID

To save space, mode/sub-mode IDs are all abbreviated.  In the first example above, the abbreviation is for “OLIVIA 8/500”.  In the third, the ID is for “DOMINOEX 22”.  In the second example the brief text message “CQ CH” is all that is displayed before the actual digital transmission (my call 3 times) is sent using DOMINOEX 22.  In the third example both the text message “CQ CH” and the mode ID “DM22” are displayed before the actual digital transmission is sent.  Pretty neat, huh?

Fldigi gives you complete control over video ID/Text in the Configure/ID/Video menu:

As with the other menus, you will need to read the manual to understand all of the various features, but if all you wish to do is send video Mode ID, the settings in the menu above should work.

SUMMING IT ALL UP:

RSID and Video ID/Video Text have been around for a long time, but have not yet been used much by county hunters.  That is unfortunate because they can be very useful tools.  Just as an example, I have come up with a scheme where a mobile (putting out digital counties) might use these tools in their initial CQ call and in their CQ call every time they change modes.  Their signal (assuming they begin by using PSK-63 would look like this:

The video text would assure other folks that this is a county hunter calling CQ.  The next line (Video Mode ID) would tell people that the mobile is using PSK-63.  The next line is the mobiles RSID which would pop up the notification box for watchers telling them again the mode plus the offset.  If the watcher wishes, they can click on the “Go To xxxx” button and instantly be on the correct mode and tuned to the mobile’s frequency ready to work them.  The CQ-CH macro would control things so that the only time the IDs, etc. are transmitted would be when the mobile calls CQ. To insure that other macros will NOT transmit RSID or any Video ID/Text, you must have these features configured, but turned OFF in the Configure/ID/RsID and Configure/ID/Video menus.

If you would like to have the complete macro file containing this feature, you can get it at: https://dl.dropboxusercontent.com/u/26171574/Fldigi%20Macros/CountyHunter%20Mobile%20RSID%20Video.zip

If you would like a complete set of macro files (Zipped) that I use then go here: https://dl.dropboxusercontent.com/u/26171574/Fldigi%20Macros/Fldigi%20Macros%2003-28-2014.zip

You should place these macros (and any others you may be using) in the following folder: “C:\Users\(Your name/call)\fldigi.files\macros”

THE FUTURE:

I challenge other people in the digital county hunter community (fixed or mobile) to experiment with these new tools.  There are bound to be better ways to use RSID and Video ID/Text to make digital county hunting more efficient and fun.  I will be happy to look at and share any ideas you may have in future Digital Happenings articles.

March Activities:

Digital activities during March stayed at a high level!  Digital county hunter mobiles spotted on W6RK in March and a very rough count of each’s total counties/modes are:
W0NAC			 4
K5YAA			 6
KW1DX			12
NA8W 			33
W5QP 			 6
WQ7A				 3
NA8W/WD8BAH		12

The updated Table 3 is given below:

Please note that WD4OIN has also joined the small group of those who have completed 50% or more of the 5 – Mode Award.  Congratulations Jack!

How To Get Your 5 – Mode Statistics Updated:

Several past Digital Happenings articles have given detailed instructions on a new and easy way to update your digital statistics for Table 3 by using a small program called “Digital Report Utility”.  This new program will create a report for you showing your progress for both the USA – Digital and the 5 – Mode Awards and email it to W0NAC.  Instead of repeating these instructions every month I have included them in a Microsoft Word document that you can download by clicking on the following link: https://dl.dropboxusercontent.com/u/26171574/Happenings/5%20Mode%20Update.doc

Other possible topics for future months include (in no particular order):

“Compatibility Issues When Making RTTY Contacts”
“How To Log Your Digital Contacts In Logger”
“Macros – Revisited”
“New Digital Awards?”
“Digital Software Installation – Revisited”
“Award Difficulty Index”

I hate to keep harping at you all, but I really need (and welcome) your suggestions on topics for future articles!  Or, if you have a story or tip that you wish to contribute, I will certainly try to include it.  Short stories describing your experiences/joys/frustrations/etc. in getting started in digital ops would be especially welcome.  Summaries of any digital trips you make (or have made in the past) would also be good.  I look forward to hearing from you. Don’t be shy!

Please email me with your comments/suggestions at w0nac@comcast.net and don’t forget to send your updated status for the USA – Digital and 5 - Mode Awards  so I can update the Active Digital County Hunters Award Status list again next month.

73’s and we hope to see you on our waterfall again real soon!

Matt – W0NAC