SOHO CONTINGENCY SCRIPT F-05

CELIAS MTOF Power ON

(SOHO Server/Operations/Instruments/CELIAS/CELIAS CS F-05)

Version 1.0

Based on:  OCD #1683, CR #1757, MOCR# 02-0051.

Change Record:

1.0	10 Mar 09	-	Replace NRT session with f_fl_mtof_recovr procedure.

OCD#2366, CR#2548, MOCR#09-0028.  NJP

Positions Required:	OE (CELIAS representative must be available)

Anomaly Indications:

Script execution must be requested by CELIAS representative.

Loads:  None

Main Activities:

1.	Switch MTOF sensor to STANDBY mode

2.	Disable substitution heater

3.	Set limits and levels in DPU

4.	Bring up high voltages

Plots Required:	None

|  | Pos | Activity | Procedure |
| --- | --- | --- | --- |
| 1 |  | CONTINGENCY: If problems are encountered during MTOF turn-ON, the CELIAS representative may direct execution of the immediate standby procedure to safe MTOF. | f_fl_m_modstb |
| 2 |  |  |  |
| 3 |  | STEP 1: MTOF SENSOR TO STANDBY |  |
| 4 | FOT | IF MTOF is OFF (FSDMODM = Power Off) or (FSDSPM1 = Off) OR MTOF is in IFC mode (FSDMODM = IFC) OR MTOF is in manual mode (FSDMODM = Manual) OR MTOF is in nominal mode (FSDMODM = Nominal) Run procedure to switch MTOF to standby mode. | f_fl_m_modstb |
| 5 |  |  |  |
| 6 |  | When MTOF is in Standby mode (FSDMODM = Standby) request CELIAS representative check the limits and levels stored in the DPU. |  |
| 7 |  |  |  |
| 8 |  | STEP 2: DISABLE SUBSTITUTION HEATER |  |
| 9 |  | Disable MTOF substitution heater, if ON (COBS thermal channel 65). | k_thc_dis (65) |
| 10 |  |  |  |
| 11 |  |  |  |
| 12 |  |  |  |
| 13 |  |  |  |
| 14 |  | STEP 3: SET DPU LIMITS/LEVELS |  |
| 15 |  | IF CELIAS representative indicates correct limits and levels are not stored in the DPU run the following procedures: - Disable all HV power supplies (input: 9) - Set HPS limit, level, and delta (inputs: 8,0,0) - Set Vf limit, level, and delta (inputs: 4,75,125,5) - Set PMEq limit, level, and delta (inputs: 2,0,0,199) - Set WEq limit, level, and delta (inputs: 3,128,128,10) | f_fl_m_disabl f_fl_m_psgen f_fl_m_psgen f_fl_m_psgen f_fl_m_psgen |
| 16 |  | Wait for CELIAS representative to verify new limits and levels. |  |
| 17 |  |  |  |
| 18 |  | STEP 4: TURN UP HIGH VOLTAGES |  |
| 19 |  | Run procedure to turn up MTOF high voltages and place MTOF into an operational state. Approximately 1 hour. | f_fl_mtof_recovr |
| 20 |  | CONTINGENCY: If problems are encountered during MTOF turn-ON, the CELIAS representative may direct execution of the immediate standby procedure to safe MTOF. | f_fl_m_modstb |
| 21 |  |  |  |
| 22 |  | RECOVERY COMPLETE |  |