RCB

National Aerospace Education Center

Flight Operations Manual

Professional Pilot Technology

Intentionally Left Blank

Control Page

FAA Acceptance

I have reviewed the contents of this manual and have found it to be accepted.

Date Accepted:

REV Control Date:

Accepted ________________________________________ Dave Green, Principle Operations Inspector CRW FSDO-09

Determining Revision Status

The “Log of Current Pages” (LOG pages), number LOG-1 thru LOG-“X”, indicates the current DATE of each page of this manual.

To determine if a page in this manual is current, compare the date on the page in question with the date listed in the LOG for that page number. If the dates correspond that page is current. The dates listed on both sides of a page will be identical even though one side of a page may not have affected by the change.

Intentionally Left Blank

FOM REVISION

This “Revisions” sheet shall be retained in your manual until receipt of the next revision. Place this sheet in your manual immediately following the “CONTROL PAGE”. Refer to the following table for a listing of permanent revisions.

RECORD OF REVISIONS

| REV. NO | REV. DATE | Initial | REV. Date | REV. DATE | Initial |
| --- | --- | --- | --- | --- | --- |
| Original | 14 Jan 09 |  |  |  |  |

INSTRUCTIONS

·          Remove and replace all revised pages (marked as “R” pages in the new LOG)

·          Insert all new pages (marked as “N” in the new log)

·          Remove and discard all deleted pages (marked “D” in the new log)

All revised or new content in the manual is indicated by a black, vertical change bar in the left margin of the pages.

Intentionally Left Blank

Flight Operations Manual

Control-1 14 Jan 09

Revisions-1 14 Jan 09

LOG-1 14 Jan 09

a.i 14 Jan 09

1 14 Jan 09

2 14 Jan 09

3 14 Jan 09

4 14 Jan 09

5 14 Jan 09

6 14 Jan 09

7 14 Jan 09

8 14 Jan 09

9 23 Feb 09

10 14 Jan 09

11 14 Jan 09

12 14 Jan 09

13 14 Jan 09

14 14 Jan 09

15 14 Jan 09

16 14 Jan 09

17 14 Jan 09

18 14 Jan 09

19 14 Jan 09

20 14 Jan 09

21 14 Jan 09

22 14 Jan 09

23 14 Jan 09

24 14 Jan 09

25 14 Jan 09

26 14 Jan 09

27 14 Jan 09

28 14 Jan 09

29 14 Jan 09

30 14 Jan 09

31 14 Jan 09

32 14 Jan 09

33 14 Jan 09

34 14 Jan 09

35 14 Jan 09

36 14 Jan 09

37 14 Jan 09

38 14 Jan 09

39 14 Jan 09

40 14 Jan 09

41 14 Jan 09

42 14 Jan 09

43 14 Jan 09

44 14 Jan 09

45 14 Jan 09

46 14 Jan 09

Intentionally Left Blank

The rules and regulations of this manual apply to all pilots, regardless of the level of certification, who are enrolled in a course of training at, or operating an aircraft owned or leased from Fairmont State University National Aerospace Education Center.

In compliance with FAR 141.93(a) (3), safety procedures and practices may be found with in this manual.

All pilots are expected to comply with more restrictive or limiting regulations found in the Federal Aviation Regulations, or any State or Local regulations, in addition to the rules and regulations of this manual.

In addition to all current FAA regulations, the following rules and regulations will apply to all students enrolled in Flight Training at Fairmont State University National Aerospace Education Center.

This manual is effective immediately. These regulations are subject to revisions and changes which can be made at anytime. Any questions or comments regarding this manual, or requests for exemptions or changes, should be directed to the Chief or Asst. Flight Instructor or Manager of Flight Operations.

Intentionally Left Blank

Table of Contents

Topic   Page

Definitions…………………………………………. 3

Section 1 Operating Rules…………………………. 6

1.1  General Information……….……….…… 6

1.2  Necessary Items For Flight Program 7

1.3 General Contact information……………..7

Section 2 Scheduling…………………………… …. 9

Section 3 Weather Limitations…………………… 12

Section 4 Dispatching Aircraft…………………. 14

Section 5 Ground Operation of Aircraft…… ………16

5.1 General………………………………….. 16

5.2  Parking Procedures………………… …..17

5.3  Taxiing Procedures……………………… 17

Section 6 Flight Operation…………………………..19

6.1 General…… … ……………....19

6.2  CKB Airport Traffic Rules…………….. 19

6.3  CKB Practice Area……………………… 21

6.4 Night Flights……………………………. 23

6.5 Solo Training Flights……………………. 23

Section 7 Cross-Country Flights………………… 26

7.1  General……………………………………26

Part 141 Approved Airports……………….. 28

7.2  VFR Cross-Country Planning…………… 29

7.3  Dual Cross-Country Flights……………. 30

7.4  Solo Cross-Country Flights……………… 31

Section 8 Winter Operations…………………… ..34

Section 9 Fuel Conservation and Mixture Leaning 35

Section 10 Penalties and Fines…………………… 36

Section 11 Non-Instructional Aircraft Rental…… 37

Section 12 Safety Procedures……………………… 38

Course Completion………………………………… 39

Conduct in Flight Rooms and Vicinity of

the Flight Office……………………….. 39

Airport Diagram…………………………………….. 40

Pre-Solo Requirements……………………………. 41

Pre-Solo Cross-Country Requirements……………. 41

End of Course Requirements……………………….. 42

Intentionally Left Blank

Terms in this publication will have the following definitions:

ADVANCED STUDENT: Any student that is working on any course beyond the Private Pilot Certification Course or any student that has their Private Pilot license.

COURSE: Division of instruction consisting of one or more phases to satisfy long term training goals.

CROSS-COUNTRY: Pilot-in-command, solo flights or dual flights involving landing(s) at airport(s) of more than 50 nautical miles distance.

DUAL: Flight instruction given to a student by a FAA certificated

flight instructor.

EVALUATION: An EXCELLENT performance occurs when a student demonstrates procedural, manipulative, and perceptual skills at least equal to the instructor.

A GOOD performance occurs when a student demonstrates procedural, manipulative, and perceptual skills approaching that of the instructor.

A FAIR performance occurs when a student demonstrates procedural, manipulative, and perceptual skills exceeding the minimum standards of acceptability.

A MARGINAL performance occurs when a student demonstrates procedural, manipulative, and perceptual skills at least equal to the minimum standards of acceptability.

An UNSATISFACTORY performance occurs when a student demonstrates procedural, manipulative, and perceptual skills which do not equal the minimum standards of acceptability.

FLIGHT MANEUVER: The flight training dimension that involves the actual piloting of an airplane.

FLIGHT TRAINING: Training and aeronautical experience used to meet requirements for a certificate or rating.

GROUND LESSON: Ground training instruction pertinent to aviation pilot education.

GROUND TRAINER: Ground training instruction utilizing an approved synthetic trainer.

FSU RAMP: The ramp located directly west of Hanger B.

FLIGHT INSTRUCTOR: An approved Fairmont State Flight Instructor currently employed in said position.

INSTRUMENT:  Flight instruction in which a student pilots the airplane solely by reference to instruments in actual or simulated conditions.

LESSON: Division of instruction consisting of one or more lesson segments to satisfy short-term training goals

LESSON SEGMENT: Division of instruction consisting of one block period.

LOCAL: Dual, pilot-in-command, or solo flight conducted within 25 nautical miles of CKB Airport

NIGHT: Dual, pilot-in-command, or solo flight conducted between the end of evening civil twilight and the beginning of morning civil twilight.

OBSERVER: A person watching the wings and the tail of the airplane, so as not to hit anything, as the pilot pushes the airplane back into the hangers.

PILOT-IN-COMMAND: Flight in which a student enrolled in the private pilot course is the sole manipulator of the airplane, or any time a student enrolled in advanced course is in control of the aircraft.

PRIMARY STUDENT: Any student that is working towards their Private Pilot Certificate.

RENTER: All persons flying Fairmont State University aircraft.

R.O.N. OPERATIONS: Remain Over Night operations are conducted when a solo cross country is inadvertently required to remain at an airport other then CKB due to weather or other limitations.

SOLO: Flight in which a student pilot is the sole occupant of the airplane. Any flight conducted without an instructor on board.

STAGE: Division of instruction consisting of one or more lessons to satisfy intermediate training goals.

STAGE CHECK: Flight in which a student demonstrates the operational procedures, flight maneuvers, and perceptual patterns for purposes of evaluation. These flights should be logged as dual and are to be included in the total time account.

STUDENT: Any person actively taking flight instruction at Fairmont State University.

Section 1. Operating Rules

1.1 - General Information

1.1.1. Students are not allowed to eat or drink in university aircraft.

1.1.2. Students are not permitted behind the main desk in the main office or in the flight instructor offices in the flight planning room without the consent of a flight instructor, Chief Flight Instructor, or administrative personnel.

1.1.3. Students must have in their possession during all flights:

a. Pilot Operating Handbook for aircraft to be flown

b. Current medical and logbook

c. Certificates or licenses where appropriate

d. Current Cincinnati sectional or sectional for route of flight

e. Student Flight Handbook

f. Headsets

g. Performance and Flight Data Sheet (weather, nav log, weight & balance)

h. Advanced Students will be required to have the following additional items:

1. Current enroute chart

2. Current approach plates

3. View limiting device (hood or foggles)

4. Instrument covers (failures)

1.1.4. SIM (Student Information Memos) will be posted in RM 131 (Flight Planning Room). All students must read and initial SIM cards in student file.

1.1.5. The Business Office expects you to maintain a credit on your flight account.

1.1.6. Each pilot is responsible for a thorough pre-flight inspection. Including, but not limited to, determination of the proper loading of the aircraft; take-off & landing distances; and fuel requirements for each flight

1.1.7. At the termination of each flight all students must contact flight instructor.

1.1.8. No aircraft will be flown until its exterior is free of ice, snow, or frost.

1.1.9. All flight must monitor NAEC Unicom frequency on 123.50 during flight training. Exceptions: 1) To comply with flight training conditions or needs. 2) One radio inoperable.

1.2 - Necessary Items for Flight Program

1.2.1. Students

• Student Flight Handbook

• Aircraft Pilot Operating Handbook

• Personal Logbook

• Cincinnati Sectional, enroute charts/approach plates

• Medical

• Flight Computer and Plotter

• Notepad and Pencil (or Pen)

• Flashlight

• Earplugs (Optional)

• Headphones

• Practical Test Standards

• Airport Facilities Directory (AFD)

1.2.2. Instructors

• Student Flight Handbook

• Aircraft Pilots Operating Handbook

• Flashlight

• Cincinnati Sectional

• Practical Test Standards

Available in Flight Planning Area

• Advisory Circulars

• FAA Safety Pamphlets

• Flight Planning Chart

• Weather Information (Telephone l-800-WX-BRIEF) and Computer with Radar

1.3 – General Contact Information

Fuel Services

V1 Services- CKB Phone Number 1-304-848-6700

FAA Medical Examiners in the Area

Dr. Govind M. Patel, MD

1844 Locust Ave

Fairmont, WV, 26554 304-366-1538

Section 2. Scheduling

2.1.1. The assigned flight instructor is responsible for all scheduling. Students are not permitted to schedule their flight training.

2.1.2. All FSU students and other students on the block time scheduling system will be scheduled in the following manner:

a. Students will be automatically scheduled for 2 lessons each week.

b. Students enrolled for flight labs will receive priority with respect to scheduling school airplanes.

c. Students will be scheduled based on certificate seniority on a first come first serve basis.

2.1.3. Scheduled flight periods or blocks function from the first day of classes, until the last day of scheduled classes for the semester. EXCEPTIONS WILL BE DURING BREAKS

2.1.4. Reporting time for all flight periods is fifteen minutes prior to flight. Any student reporting 10 minutes past schedule flight time will be considered a no show and charged per 2.1.10.

2.1.5. Students will not be allowed to schedule when their accounts are below $200.00.

2.1.6. Students must cancel any lesson they cannot make AT LEAST 12 hours prior to the time the lesson is scheduled. If the lesson is not canceled within this time, the student may be billed for the full lesson. The rates for billing on no-shows or late cancellations are listed in Section 2 #10. The Chief Flight Instructor will handle appeals on an individual basis and his decision will be final and binding.

2.1.7. Absences not reported in advance except in unusual circumstances, are considered unexcused absences. After a student has two unexcused absences, the matter will be directed to the Chief Flight Instructor. After 2 unexcused absences (no shows) students may be removed from flight training for the reminder of the semester.

2.1.8. If a student must cancel due to an emergency, it is the responsibility of the student to provide written proof of the emergency. Written proof must be provided for any consideration of a waiver from our cancellation policy. Written proof must be submitted within the next two scheduled lessons.

2.1.9. If you must stop flying for a period greater than two weeks (4 lessons), you may be removed from your current instructors schedule. Upon returning, you may be reassigned to a different instructor.

2.1.10. The billing rate for no-shows and late cancellations are as follows:

a. Dual Lesson: Students may be billed ground time and flight time for the full scheduled lesson, at the rate appropriate to their course of training. Students may also be billed at the current hourly rate for each hour that they booked an aircraft or simulator.

b. Solo Lesson: Students may be billed at the current aircraft rental rate for each hour that the aircraft was booked.

2.1.11. Students receive 3 credit hours for flight training; therefore, students are required to show at schedule flight training time regardless of whether actual flight training will take place. Flight training lab follows same procedures and rules as normal University courses. Follow class cancellation policy for University during adverse weather conditions.

Intentionally Left Blank

Section 3. Weather Limitations

3.1.1. No aircraft shall be dispatched for a solo / dual flight from Fairmont State University National Aerospace Education Center, unless the following weather conditions are maintained:

Primary Students

Local 3500ft. / 7mi. Pattern 2000ft./ 5mi. Xctry 5500ft / 10mi.

Advanced Students

Local 3000ft. / 5mi. Pattern l500ft / 3mi. Xctry  5000ft / 7mi.

• These conditions need to be reported one hour before to one hour after block time at CKB’S AWOS / Metar or TAF and at least one of the following stations: EKN, MGW, PKB, CRW.

3.1.2. The following weather minimums must be maintained for I.F.R. flight at CKB:

a. IFR solo with Chief Pilot approval: 800ft/2mi

b. IFR dual with Chief Pilot approval: 400ft/2mi.

c. No flight into known or forecasted icing conditions.

3.1.3. The following wind conditions will apply for all solo flights:

Aircraft  Max. Velocity  Crosswind Component

172   15 kts  10 kts

172RG  15 kts 10 kts

• Max. Velocity includes peak gusts.

• All students will have maximums assigned by their instructor and endorsed in student log book. These maximums cannot exceed the above listed.

3.1.4. Night flights must have conditions of: 6000ft. / 10mi. present and forecasted for all flights.

Intentionally Left Blank

Section 4. Dispatching Aircraft

4.1.1. Renters will receive keys and dispatch form from the flight office or their instructor, prior to every flight. All keys and dispatch form must be returned to a CFI at the end of each flight. At no time should a student take an aircraft that is not dispatched to him/her.

4.1.2. Flight training aircraft will only be dispatched through the Flight Schedule System (My FBO). An approved Fairmont State University Flight Instructor shall conduct all flight instruction.

4.1.3. Dispatching Priority

a. Check rides (including stage checks)

b. Dual block student’s

c. Solo block student’s

d. Dual non-block student’s

e. Solo non-block students

4.1.4. Aircraft will only be dispatched for solo lessons under the following conditions:

a. Weather minimums and max. wind are within limits

b. Student has all items as per Section 1.1.3.

c. Copy of their weight and balance calculations submitted

d. Student has received instructor approval for flight

4.1.5. All aircraft dispatched for day solo training must be on the ground by official sunset. Cross-Country flights for advanced students, however, will be allowed to return after official sunset provided the following conditions are met:

a. Student has logged night hours within the past 90 days

b. A dispatcher/instructor will be on duty to receive keys and dispatch form upon return, or approval from the flight instructor to leave the keys and dispatch form in the “mailbox” in the soft hanger.

4.1.6. Non-instructional after hour’s rentals shall return the aircraft to the ramp, tie it down, and place the aircraft dispatch form and aircraft keys in the “mailbox” in the soft hanger.

Intentionally Left Blank

Section 5. Ground Operations

5.1 - General

Please refer to the Definitions (Section 1) section for unfamiliar terms.

5.1.1. When removing aircraft from or returning aircraft to the hangers or the NAEC ramp, an observer must accompany students. At no time should a student attempt to do this alone unless authorized by an instructor.

5.1.2. On the NAEC ramp, aircraft should be positioned beyond the engine operating area prior to aircraft starting.

5.1.3. Prior to aircraft startup, make sure that the pitot cover; cowl plugs; control wheel lock; and tow bar have all been removed and properly stowed inside the aircraft.

5.1.4. Prior to starting the engine and for engine starting, all pilots should refer to the checklist included in the airplane.

5.1.5. At no time while the aircraft engine is running should anyone enter or exit the aircraft. Exceptions to this rule are in Section l2.1.l.

5.1.6. During the refueling of any aircraft, all persons in the aircraft must deplane and maintain a safe distance from the aircraft.

5.1.7. After each flight the aircraft must be properly secured. A properly secured aircraft will have the following items completed:

a. Aircraft tied down or returned to the hanger and locked

b. Gust lock installed

c. Cowl plugs installed (if available)

d. Pitot tube cover installed

e. Aircraft times recorded in Flight log

5.1.8. Pilots shall report any malfunctions or aircraft damage to a Certified Flight Instructor, in writing, on the proper maintenance forms. The CFI will then record the squawk on the maintenance squawk sheet. The flight office will then record the squawk in the maintenance system and aircraft flight log book.

5.2 — Parking Procedures

5.2.1. All aircraft are to be parked on the ramp or in the hanger in appropriate slots with their propellers set in a horizontal position, and tow-bars removed and stowed in the aircraft or equipment area.

5.2.2. Close, latch, and lock all doors, windows, and baggage doors on the aircraft upon deplaning.

5.2.3. At no time is a student to pull out, or push back an aircraft from the hanger or tie-down spot without the assistance of an observer.

5.3 - Taxiing Procedures

5.3.1. No person shall taxi an aircraft until he/she has ascertained that there will be no danger of collision with any persons or objects in the immediate area.

5.3.2. All aircraft shall be taxied at a safe and reasonable speed with due regard for other aircraft, persons, and property.

5.3.3. Aircraft awaiting take-off shall stop at the hold short line or at least 100 feet (unless usable area does not permit) from the runway in use and in a position so as to have a direct view of aircraft approaching for landing.

5.3.4. All aircraft shall be taxied in the center of the taxiways.

5.3.5. Taxiing on sod is prohibited without special written authorization from the flight office.

5.3.6. At no time during taxi will any activity not related to taxing the aircraft be conducted during taxi operations.

Intentionally Left Blank

Section 6. Flight Operations

6.1 – General

6.1.1. Primary students shall perform all take-offs at CKB using the full length of the runway.

6.1.2. Advanced students may perform intersection takeoffs at the following taxiways: Departing 21, taxiway F; Departing 3, taxiway B

6.1.3. Passenger carrying is prohibited on all training flights except for observer students authorized by the Chief Flight Instructor.

6.1.4. No formation flying is allowed.

6.1.5. IFR flights into known or potential icing situations are prohibited.

6.1.6. Intentional spins are prohibited in the Cessna 172RG and the BE-76 Duchess. Intentional spins in the Cessna 172 must meet P.O.H. requirements.

6.1.7. Primary solo flights of any nature are not to be conducted unless a NAEC flight instructor is physically present at NAEC. Operating in the local area while monitoring the school frequency or C.T.A.F frequency, shall be construed as physical presence (exceptions need Chief Pilot, or Assistant Chief Pilot approval).

6.1.8. All flights must land with a minimum of 45 minutes of fuel reserve.

6.1.9. All flights must take-off and depart only from airports that meet the minimum safe runway lengths prescribed by the aircraft P.O.H. for the day and type of flight being conducted.

6.2-Clarksburg Airport Traffic Rules

6.2.1. The traffic and taxi rules for CKB Airport are to be observed at all times.

6.2.2. Use of the Tower / C.T.A.F. is required for all maneuvers in the traffic pattern, and around the traffic area.

6.2.3. Pilots of Fairmont State University aircraft are urged to report to CKB Tower when a) leaving the traffic pattern, b) entering the traffic pattern, c) while in the pattern.

6.2.4. Landings and take-offs shall be made directly into the wind, or the runway most nearly aligned with the wind (active runway). When the wind is light/calm, take-offs and landings shall be conducted on the active runway.

6.2.5. When landings or take-offs are made in a direction other than as described in 6.2.4, the pilot is solely responsible for determining that the operation can be completed with safety and without interference with, or disruption of other traffic in the area. Such landings/take-offs are not authorized for convenience and shall be made only for legitimate reasons, such as crosswind take-off and landing instruction, use of a longer runway for heavily loaded or large aircraft, etc.

6.2.6. Turns shall be made after take-off only after the airport boundary has been reached and the aircraft has attained an altitude of at least 1700 feet MSL (500 AGL) and it has been ascertained there will be no danger of collision with other aircraft.

6.2.7. Aircraft intending to remain in the traffic pattern shall climb to traffic altitude of 1000 feet AGL (2200 feet MSL)

6.2.8. Aircraft entering the traffic pattern shall exercise caution and courtesy so as not to cause aircraft already in the pattern to deviate from their course.

6.2.9. Landing traffic shall land only if the active runway is clear of all traffic.

6.2.10. These rules do not eliminate or affect in any way the requirements of the Federal Aviation Regulations for securing an air traffic clearance for any flight conducted within the Class C or D Airspace at any time when the ceiling or visibility conditions are below those required for visual flight.

6.3 - CKB Practice Area

6.3.1 The practice area’s for local flights of Fairmont State University aircraft lies within a 15 nautical mile radius of the geographic center of CKB Airport (see next page).

6.3.2 Except for the purpose of take-off or landing, the practice area extends from 500 feet above the surface or 1000 feet above the highest obstruction within a city, town, village, or settlement. Otherwise Fairmont State aircraft may fly up to 10,000 feet MSL within the practice area. In addition unless receiving instrument instruction, pilots should avoid the instrument approach courses, centerlines of VOR airways, and the Clarksburg Class D Airspace.

6.3.3. KEEP YOUR DISTANCE FROM ALL OTHER AIRCRAFT AT ALL TIMES

6.3.4 All pilots are responsible for collision avoidance. The area must be clear of other aircraft prior to initiating any training maneuver. Be certain to clear the area thoroughly before beginning a maneuver.

6.3.5 All flights will monitor CKB Tower / Approach Control (121.15) when operating in the local area outside the traffic pattern.

PRACTICE AREAS

6.4 - Night Flights

The following additional limitations shall apply to all night flights.

6.4.1. Aircraft must be equipped with an operative landing light, navigation lights, rotating beacon and/or wing tip strobe lights.

6.4.2. Surface Temperature 10F / -12C or warmer for dual or 20 F / -7C solo.

6.4.3. Any renter wishing to do a solo night flight must have logged 3 take-offs and landings to a full stop within the past 90 days with the University.

6.4.4. Renters who have not logged the appropriate time (see 6.4.3) within the past 90 days will be required to receive a night checkout by a flight instructor.

6.5 - Solo Training Flights

6.5.1. The instructor to whom the student is assigned must specifically approve all local solo training flights.

6.5.2. Except for unexpected weather, aircraft emergencies, or Cross-Countries primary solo students may only make landings at the CKB Airport unless otherwise endorsed.

6.5.3. Crosswind take-offs and landings, on other than the active runway, will be practiced by students only with the permission of the instructor/dispatcher in charge.

6.5.4. Simulated emergency operations may only be practiced with an instructor aboard the airplane.

6.5.5. If an emergency landing occurs, the pilot must notify the school immediately (call 304-842-8300) and MAKES NO ATTEMPT TO FLY THE AIRCRAFT unless specific approval is given.

6.5.6. All students must carry their student or pilot certificate, current medical and logbook while flying (see 1.1.3).

6.5.7. Fairmont State Students are not allowed to carry passengers on any training flight or solo flight unless the Chief Flight Instructor has approved a passenger to be on board.

6.5.8 Except for take-off, landing and emergency landing practice, students will operate their aircraft at least 2500 feet AGL, unless lower altitude is required to meet the PTS (Ground Reference Maneuvers).

Intentionally Left Blank

Section 7. Cross-Country Flights

7.1 - General

7.1.1. All students scheduled for Cross-Country flights should arrive at the flight office at least thirty minutes prior to their scheduled flight. This time should be used for updating weather, and finishing all planning.

7.1.2. The following items must be completed no later than thirty minutes after the time the aircraft is scheduled:

a. Copy of flight plans submitted to dispatcher

b. Preflight inspection

c. Received signoff from CFI

d. Sectional, and flight planning sheet to CFI

e. Flight plans on file with Elkins FSS

7.1.3. All students are required to file a flight plan and submit a copy to their CFI. The flight plan must be completed in full and contain the following information:

a. Intended route

b. Planned departure and arrival times for each leg

c. Fuel consumption for each leg

d. Checkpoints and distances

e. Cloud coverage at departure and destination points

f. Winds aloft and surface winds at planned airports

g. Weather forecast enroute for each leg

7.1.4 All students are required to file, open, and close flight plans for each leg or round trip of the Cross-Country flight.

7.1.5 Students shall not fly close enough to one another on Cross-Country training flights to see each other.

7.1.6 All solo flights shall depart on a Cross-Country flight with full fuel tanks.

7.1.7. All aircraft must return to CKB with at least 45 minutes of fuel remaining. All landings at Cross-Country airports must be with at least 45 minutes of fuel remaining

7.1.9. Cross-Country training flights may only go to airports that meet the requirements and approval of the Part 141 operations Manual approved by the FAA. See flight instructor for more detail’s or questions.

PART 141 APPROVED AIRPORTS

-Private Pilots are limited to the BOLD cities only.

-No Private airports allowed.

West Virginia

Beckley (BKW)

Buchannon (W22)

Charleston (CRW)

Clarksburg (CKB)

Elkins (EKN)

Fairmont (4G7)

Huntington (HTS)

Lewisburg (LWB)

Martinsburg (MRB)

Morgantown (MGW)

Parkersburg (PKB)

Phillipi (79D)

Sutton (48I)

Wheeling (HLG

Virginia

Pennsylvania

Pittsburgh (AGC)

Hagerstown (HGR)

Washington (AFJ)

Rostraver (FWQ)

Latrobe (LBE)

Ohio

Akron (CAK)

Circleville (CYO)

Columbus (CMH)

Columbus (LCK)

Columbus (TZR)

Mansfield (MFD)

Zanesville (ZZV)

Roanoke (ROA)

7.2 - VFR Cross-Country Planning

7.2.1 Prior to starting VFR Cross-Country planning, the student pilot should have the following items:

a. Current sectional charts

b. Plotter

c. Flight computer

d. Pencil/pen

e. Airport/Facility Directory

f. Fairmont State X-C planning sheet.

7.2.2 Develop a flight plan utilizing one of the navigation techniques: Radio navigation, Dead Reckoning, or Pilotage. NOTE: Straight-line distance must be more than 5ONM, 100NM, or 250NM as the case may be, for FAR 61 Cross-Country requirements. It is suggested to use a large pencil to draw the line for the X-C. This way the line can be erased when the trip is finished and the chart will not become cluttered with unnecessary and often confusing course lines.

7.2.3 Measure the distance in nautical miles. Be sure to use the correct side of plotter and check scale on plotter with scale on map.

7.2.4 Measure the true course.

7.2.5 Determine the magnetic course.

7.2.6 Determine highest obstacle 4NM on either side of course.

7.2.7 Determine checkpoints. Some advice concerning the determination of checkpoints: Everything a pilot sees on the ground, which is also on the sectional chart, is a checkpoint. Checkpoints used for the determination of ground speed estimates should normally be prominent landmarks, such as 4 lane highways, large lakes, larger cities, roads and railroads running together, etc. An initial ground speed check should be made within approximately 10NM of the departure point. This check should be made after reaching cruise altitude. After this, a ground speed should be made approximately every 50NM.

7.2.8 Consult Sectional Chart Bulletin in the Airport/Facility Directory.

7.2.9 Obtain all frequencies from the Airport/Facility Directory.

7.2.10 Obtain all other airport information from the Airport/Facility Directory.

*NOTE.. Steps 1 through 10 should be done in advance of the day of the flight.

7.2.11 Call FSS. Inspect the surface analysis chart, weather depiction chart, radar summary chart and the low-level prog. chart. Also, get all applicable sequence reports, notams, terminal forecasts, area forecasts, winds aloft forecasts, airmets, sigmets, convective sigmets and the latest radar weather information.

7.2.12 Using the information from FSS, determine if the weather will permit the flight.

7.2.13 If the weather will permit the flight, determine cruising altitude.

7.2.14 Using the power charts for 75%, determine T.A.S, fuel flow, and RPM necessary for 75% power.

7.2.15 Determine ground speed, estimated time en-route, and magnetic heading. It is suggested that cruise ground speed be used for the entire distance, adding two minute for each 1000 feet of climb and five minutes for each approach and landing, to determine estimated time en-route.

7.2.16 Determine total fuel used and remaining fuel on landing. All solo Cross-Countries must depart CKB Airport with full fuel and land with a minimum of 45 minutes fuel reserve.

7.2.17 Calculate the weight and balance data.

7.2.18 Determine take-off and landing distances. Minimum runway length for solo operations is 3500 feet (see Sec. 7 #9).

7.2.19 File a flight plan.

7.3 - Dual Cross-Country Flights

7.3.1. Dual Cross-Country flights are at the discretion of the instructor.

7.3.2. Primary student Cross-Country flights shall be planned so as to remain in VFR conditions at all times.

7.4 - Solo Cross-Country Flights

The criteria for solo Cross-Country flights are as follows:

7.4.1 Minimum conditions reported and forecasted for the route and surrounding weather stations as listed in the Student Rules and Regulations.

7.4.2  No precipitation, fog, or thunderstorms are reported or forecast.

7.4.3 A temperature/dew point spread of at least 5°C steady or improving.

7.4.4 Surface wind velocity as listed in Student Rules and Regulations.

7.4.5 Surface temperature is 10°F / -12°C or above. (May be waved on an individual bases by the Chief Pilot or Assist. Chief Pilot.)

7.4.6 If conditions become less than the aforementioned required minimums, perform the most practicable alternative:

a. Return to Clarksburg Airport.

b. Return to the last point of departure.

c. Land at the nearest suitable airport

7.4.7 A separate flight plan is to be filed, activated, and cancelled at the appropriate times for each leg of the flight.

7.4.8 All primary Cross-Country flights must be endorsed in accordance with the FAR’s.

7.4.9 If a student becomes lost - assuming weather and fuel permit, climb to 6000 - 7000 feet AGL and contact the nearest Flight Service Station or controlling center.

7.4.10. In the event a primary solo Cross-Country flight is interrupted and the pilot must remain over night at another airport, the flight may not be continued without authorization of a Flight instructor / Dispatcher. Such authorization may be given by telephone immediately prior to departure.

7.4.11. If it is necessary to remain overnight, the following procedures are to be followed:

a. Secure the aircraft, preferably in a hangar.

b. Close flight plan.

c. Call flight office at 304-842-8300 or Instructor immediately.

d. Any expense, meals, motel, transportation, etc. will be the responsibility of the student

e. Prior to re-dispatch, the student must call the flight office and obtain approval for take-off from the Chief Pilot, and Instructor, or the Dispatcher.

7.4.12. All solo Cross-Country flights must have the appropriate written forms filled out before departing from NAEC. The student will present a hard copy of the flight log, and weather to the Instructor checking out the Cross-Country flight.

7.4.13 Solo flight training Cross-Countries may not be taken to a student’s hometown.

7.4.14 Fuel purchased at other airports will be credited towards your flight account, provided a written receipt is received upon return from the Cross-Country flight.

7.4.15 It is preferred that a student not go to an airport more than one time during all their solo Cross- Country flights. There are occasions when this is necessary. However a student will not go to an airport more than twice in solo Cross-Country flights except in an emergency.

Intentionally Left Blank

Section 8. Winter Operations

8.1.1. Temperature Limitations: No flights will be allowed below the following temperatures:

a. Day

1. Dual:0°F/-17°C

2. Solo: 10°F/-12°C

b. Night

1. Dual: 10°F / -12°C

2. Solo: 20F / -9°C

8.1.2 Iced, snow or frosted over aircraft will only be dispatched after all visible ice, snow, or frost has been removed from the aircraft

8.1.3 Checklists, credit cards, school ID’s, ice scrapers, etc. Shall not be used to remove ice/frost from the aircraft windscreen or control surfaces.

8.1.4. When temperatures fall below 40°F aircraft shall be properly preheated prior to flight.

8.1.5. No aircraft may takeoff with snow, ice, frost, or any other contamination adhering to aircraft surfaces.

8.1.6. Supplemental Pre-Heat Table

a. Following table shows approximate heat times to bring engine to acceptable starting temperature.

b. Note: min refers to minutes.

35°  30° 25° 20° 15° 10° 5°

| Oil Pan Heater | 15 min | 15 min | 20 min | 20 min | 25 min | 25 min | 30 min |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Engine Cowl Heater | 5 min | 5 min | 10 min | 10 min | 15 min | 15 min | 15 min |

Section 9. Fuel Conservation and Mixture Leaning

9.1.3 Aircraft should be leaned on all flights, rich for maneuvers.

9.1.2 Leaning of aircraft shall be accomplished only after proper instruction.

9.1.3 Refer to the Procedures Manual or your instructor for steps for proper leaning.

Section 10. Disciplinary Procedures

10.1 – Penalties and Fines

10.1.1 Operating an aircraft in a careless or reckless manner will result in the denial of aircraft rental.

10.1.2 Any student found in violation of any rule or regulation may receive the following, but not limited to, from the disciplinary committee:

a. Verbal warning that will be recorded in personal file

b. Written warning

c. Suspension from program as determined by the Chief Flight Instructor

10.1.3 Fines for breaking NAEC or FAA rules and regulations may be assessed to the student.

10.1.4. Other

a. Duplication costs of lost keys are responsibility of the student.

b. If master switch is left on and the battery must be replaced, the cost of the battery and labor will be assumed by the last registered student: approximate cost is three hundred dollars.

Section 11. Non-Instructional Aircraft Rental

11.1.1 Any flight time accumulated on non-training flights cannot be counted towards completion of Fairmont State University courses.

11.1.2 Flight lessons will take priority over all non-instructional aircraft rentals. In the event that an aircraft is needed for a lesson, the non-instructional rental may be canceled.

11.1.3 Any request for extended (more than one day) rentals must be submitted at least one week prior to the first day scheduled and be approved by the Chief Flight Instructor, or Assistant Chief Flight Instructor.

11.1.4 Any non-instructional aircraft rental is subject to Fairmont State University’s aircraft rental policy. If you are unfamiliar with this policy, please check with your instructor, Assistant Chief Flight Instructor or Chief Flight Instructor.

Section 12. Safety Procedures

12.1.1 The aircraft engine must be shut down when entering and exiting aircraft, except in the following

instances:

a. An instructor exiting an aircraft for student solo

b. An instructor assisting in the startup of an aircraft

c. A mechanic entering or exiting for troubleshooting purposes.

12.1.2. In an emergency, the following personnel should be contacted in the order listed below:

a. Fairmont State Flight Dispatch Office 304-842-8300

b. Chief Flight Instructor 304-629-5850

c. Assistant Chief Pilots 304-612-7631 Your Flight Instructor — number provided by CFI

FIRE PRECAUTIONS - IN CASE OF FIRE

In the Aircraft -

Follow the procedures as described within the aircraft pilots operating handbook. Fire extinguisher is located between front seats. Emergency personnel should attempt to extinguish an aircraft fire.

In the Robert C. Byrd Aerospace Center

Contact the Bridgeport Fire Department at: (304) 842-7227 or 911

Fire Extinguishers are located at following positions:

COURSE COMPLETION

Each student and instructor should pace themselves during the progress of a flight course so that the student completes the Private Pilot Certificate by the end of the Freshman Year; the Instrument Rating by the end of the Sophomore Year; the Commercial Certificate by the end of the Junior Year and the CFI and the Multi-Engine Rating by the end of the Senior Year.

Extra flying approved by a student’s own flight instructor is desirable.

CONDUCT IN FLIGHT ROOMS AND IN THE VICINITY OF THE FLIGHT OFFICE

The flight planning area is a classroom. Students making it into a social club will be asked to leave.

No loitering is allowed in the instructional offices. Because of limited space, please remain only during pre-flight and post-flight briefing or when you consult with an instructor.

AIRPORT DIAGRAM

Pre-Solo Requirements

• Aircraft systems and V-Speeds

• ATC phraseology and clearance compliance

• Carburetor heat use

• Communications failure

• Crosswind procedures

• Electrical failure

• Emergencies

• Engine failure

• FAR part 91 regulations

• Fuel requirements

• Light gun signals

• Local radio frequencies

• Location of panel instruments and controls

• Minimum safe altitudes

• Partial power failure

• Pattern and go around procedures

• Pre-flight and run-up procedures

• Required documents

• Right of way rules

• Solo requirements and privileges

• Transponder usage

• VFR weather minimums

• Wake turbulence avoidance

• Maneuvers per 61.87 (d)

Pre-Solo Cross-Country Requirements

• Cross-Country planning procedures

• Flight computer use

• Flight Service Services

• Leaning procedures

• Lost communications procedures

• Operational limitations

• Performance charts

• Pilot responsibility for pro-f light planning

• Plotter use

• Sectional chart interpretation

• Transponder usage

• VOR / GPS usage

• Weather interpretation

• Weather reports

• Weight and balance computations

Private Pilot End of Course Requirements

1. Completed FAA application form 8710 or IACRA

2. FAA Knowledge Test results

3. At least a third class FAA Medical Certificate

4. Fairmont State University Grade Sheet

5. Flight Time Requirements as follows:

6. A properly completed logbook, including:

a. All page lines accurately and completely totaled.

b. All signoffs, required by the FAR’s, completed

Part 61 Ops  Part 141 Ops

Total Flight Time   40 Hours 35 Hours

Total Dual Flight Instruction 20 Hours  20 Hours

Cross-Country Time   3 Hours    3 Hours

100NM Night XCountry   X  X

Night Training    3 Hours  3 Hours

10 T/O Landings   X  X

Instrument Training   3 Hours  3 Hours

Test Preparation (Last 60 Days) 3 Hours  3 Hours

Solo Flight Time

• 3 T/O & Landing at a Controlled airport X X

• Cross-Country Time    5 Hours     ---

• 150/100 (6 1/141) NM total to 3 Airports. 1 segment longer the 50 NM.

.

Instrument Pilot End of Course Requirements

1. Completed FAA application form 8710 or IACRA

2. FAA Knowledge Test results

3. At least a third class FAA Medical Certificate

4. Private Pilot License

5. Fairmont State University Grade Sheet

6. Flight Time Requirements as follows:

7. A properly completed logbook, including:

a. All page lines accurately and completely totaled.

b. All signoffs, required by the FAR’s, completed

Part 6l Ops Part 141 Ops

• P.I.C. Cross-Country Time 50 Hours

• Instrument Time (Actual or Simulated) 40 Hours  35 Hours

• Simulator Time allowed  20 Hours 14 Hours

• Instrument Training (CPU) 15 Hours 15 Hours

• Test Prep (within 90 days) 3 Hours 3 Hours

• 250 NM Cross-Country with 3 different X X

Approaches at 3 different Airports. At least 1 leg 100 NM.

Commercial Pilot End of Course Requirements

1. Completed FAA application form 8710 or IACRA

2. FAA Knowledge Test results

3. At least a third class FAA Medical Certificate

4. Private Pilot License with Instrument Rating

5. Fairmont State University Grade Sheet

6. Flight Time Requirements as follows:

7. A properly completed logbook, including:

a. All page lines accurately and completely totaled.

b. All signoffs, required by the FAR’s, completed.

Part 61 Ops Part 141 Ops

Total Flight Time   250 Hours  120 Hours

Total Dual Flight Instruction 100 Hours  50 Hours Instrument Training 10 Hours 5 Hours

Complex Training 10 Hours 10 Hours

100 NM Straight-Line VFR Day X-C 2 Hours 2 Hours

100 NM Straight-Line VFR Nite X-C 2 Hours 2 Hours

Test Prep     3 Hours 3 Hours

Total Solo Flight

PlC in Aircraft 50 Hours

Cross-Country PlC. 50 Hours

In Aircraft 10 Hours

Night      5 Hours 5 Hours

10 T/O & Landings at Towered Airport

3 Leg Cross-Country with one leg at least 300 Total Dist. 250 Total Dist.

Left Intentionally Blank

Left Intentionally Blank

I certify that I have read the Fairmont State Student Handbook and understand the regulations and procedures and agree to the terms outlined within. I also agree to comply with all Federal Aviation Administration regulations.

Print Students Name: ___________________________

Signature: _____________________________

Date: __________________________