ISyE 3104: Introduction to Supply Chain Modeling: Manufacturing and Warehousing

Instructor: Spyros Reveliotis

Summer 2002

Homework #3

Due Date: Friday, 6/21/02

Reading Assignment:

- From your textbook

  - Chapter 7 on process strategy and capacity planning

  - It is also advisable to read the supplement of Chapter 7 on the technologies currently used by Operations Management

- Material posted on the library reserves on the layout types

- Slides of class layout types, technology selection and capacity planning

Problem set:

- Chapter 7:

- Discussion Questions: 1,2,4,10

- Problems 5,6,8,10,11,13,14,15,27 and 35 (Hint: for problem 13 use the linear regression theory you learned in your statistics class to build a function: Units produced at year t = at+b , based on the provided data; refer also to the solution of the extra credit problem in Homework 2.)

- Case Study on Shouldice Hospital

Chapter 7		Process Strategy and Capacity Planning

DISCUSSION QUESTIONS

1.	(a)	Some advantages of standardization are:

- Equipment can often be special purpose rather than general purpose, leading to increased operational efficiency

- Equipment operators may be less highly skilled

- Work orders and job instructions are typically fewer

- Raw materials inventory is usually lower, since the fact that the same material is used in the production of more than one items implies a lower variability in the experienced demand (an effect known as variability reduction due to “pooling”)

- Ratio of work-in-process inventory to output is usually lower

- One can often “produce to stock”, since the chances that a standardized item becomes obsolete/outdated are less than those for a more specialized unit.

- Scheduling is usually simpler because of the reduced number of standardization of machine routings

- Quality control is usually more readily accomplished

- We typically obtain variety while maintaining a degree of standardization by following a modular strategy where specific standard modules are assembled to get a quasi-custom product.

2.

| Product | Likely Process |
| --- | --- |
| Beer Business Cards Automobiles Telephone “Big Mac” Custom Homes | Product Focused/Continuous Process Focused/Job Shop Modular/Repetitive Modular/Repetitive Modular/Repetitive Jop Shop with components made in Product Focused and Modular facilities |

- Products produced by a repetitive process include virtually all assembled items (i.e., automobiles, motorcycles, home appliances, computers, etc.)

10.	The assumptions of the net present value technique are:

  - Interest rates are known for the entire term of the investment

  - Payments are made at the end of each time period

  - Investments with similar net present value are similar in other respects (at least, we make this assumption if net present value is the only method of evaluation of investment used)

PROBLEMS

  - utilization = actual / design capacity = 5,000 / 7,000 = 0.7143 ( 71%

  - efficiency = actual / effective capacity = 4,500 / 5,000 = 0.9 ( 90%

7.8	effective capacity = actual (planned) output / designed capacity ( 0.93 = 800/ designed capacity (

designed capacity = 800/.93 = 860

  - anticipated output 	= (Design capacity) x (Effective capacity) x (Efficiency)

= 108 x 0.80 x 0.90 = 77.76 ( 78 chairs

  - 8 hr x 5 days x 2 shifts x 4 machines x 0.80 x 0.95  =  320 x 0.80 x 0.95 = 320 x 0.76 = 243.2

243.2 / 4 = 60.8 std. hrs. for each machine

7.13	We shall interpolate the data provided below through a linear function: Y= a+b*X, where the function parameters a and b will be estimated through the standard linear regression theory.

| Year | X | Y | X2 | XY |
| --- | --- | --- | --- | --- |
| 1991 1992 1993 1994 1995 1996 1997 1998 1999 2000 | 1 2 3 4 5 6 7 8 9 10 | 15.00 15.50 16.25 16.75 16.90 17.24 17.50 17.30 17.75 18.10 | 1 4 9 16 25 36 49 64 81 100 | 15.00 31.00 48.75 67.00 84.50 103.44 122.50 138.40 159.75 181.00 |
|  | ∑X = 55 | ∑Y = 168.29 | ∑X2 = 385 | ∑XY = 951.34 |

| Regression Output |
| --- |
| Constant Std err of Y est R squared No. of observations Degrees of freedom | 15.11266 0.301804 0.216841 10 8 |

X Coefficient = 0.312060, Std err of coef. = 0.033222

X bar  =  ∑X / n  = 5.5

Y bar  =  ∑Y / n  = 16.829

b         =  25.745 / 82 = 0.312060

a         =  16.829 – 0.312 x 5.5 = 15.11266

Year 2001 = a + bx11, therefore

15.11 + 0.312 x 11 = 15.11 + 3.43 = 18.54

Year 2003 = a + bx13, therefore

15.11 + 0.312 x 13 = 15.11 + 4.056 = 19.16

Year 2007 = a + bx17, therefore

15.11 + 0.312 x 17 = 15.11 + 5.3 = 20.41

(a)	2001 capacity needs = 18.54

2003 capacity needs = 19.16

2007 capacity needs = 20.41

(b)  	Requirements in 2003 are for 19.16 lenses, therefore, River Road Medical Clinic will need 8 machines ( 19,160/2,500) = 7.66; round up to 8)

7.14	In 2001 River Road Medical Clinic has 8 machines @2500.  In year 2007 they need capacity of 20,410.

(a)  	Therefore, if they add 5,000 to capacity in 2001 total capacity in 2007 will be 25,000 lenses, more than adequate.  Exceeds by 4,590.

(b)	If they buy the standard machine in 2001, their capacity in 2007 will be 22,500 lenses still more than adequate; the smaller machine will suffice.  Exceeds by 2,090.

Notice that the above suggestion adopts the typical approach of maximizing the expected profit. Another, more conservative approach would be to pick the option that maximizes the worst-case outcome. In that case, the small line would be the selected option, since it guarantees a net profit of $100,000 even under an unfavorable market condition. The criterion to be optimized at each case depends on the considered situation, and essentially reflects the philosophy/attitude of the decision-making team with respect to risk-taking. However, no matter which criterion is used, the information provided by the decision-tree can help structure the decision-making process.

7.27

(b) At 3,000, C is best

(c) Between 1,600 and 2,400, B is best

7.35

| Expense | Machine A | Machine B |
| --- | --- | --- |
| Original cost Labor per year Maintenance per year Salvage value | 10000 2000 4000 200 | 20000 4000 1000 7000 |

| Machine A |
| --- |
| Year |  |  | NPV Factor* | NPV |
| Now 1 2 3 | Expense Expense Expense Expense | 10000 6000 6000 6000 | 1.000 0.893 0.797 0.712 | -10000 - 5358 - 4782 - 4272 |
| 3 | Salvage revenue | 2000 | 0.712 | -24412 + 1424 |
|  |  |  |  | -22988 |

* NPV factor from Table 7.4

| Machine B |
| --- |
| Year |  |  | NPV Factor* | NPV |
| Now 1 2 3 | Expense Expense Expense Expense | 20000 5000 5000 5000 | 1.000 0.893 0.797 0.712 | -20000 - 4465 - 3985 - 3560 |
| 3 | Salvage revenue | 7000 | 0.712 | -32010 + 4984 |
|  |  |  |  | -27026 |

* NPV factor from Table 7.4

NPV for machine A is -$22,988; NPV for machine B is -$27,026.  Therefore, Machine A should be recommended.

CASE STUDY

- Shouldice beds are only fully utilized four days per week, but doctor operate five days: so the question of utilization has at least these two perspectives.

Utilization = actual/design = 450 / (90*7) = 71%

- Per the table below, if surgery is added on Saturday and held at 30 per day, then added beds are wasted capacity. Beds are available on Saturday under current operating policies.

Utilization = 540 / (90*7) = 85.7%

3.

- If beds are increased by 50% (to 135) but surgery is held at 30 per day, the added capacity is wasted.

- With the added beds, surgeries could move from 30 per day to 45 per day.

- A 50% increase in bed capacity needs to be matched with 45 surgeries Monday, Tuesday, Wednesday, and Thursday to fully utilize facilities 4 days per week.

- If 30 surgeries are performed each day in 5 rooms, then 6 are performed in each room. To perform 45 per day, the rooms will need to be occupied 9 hrs per day or more rooms will need to be added. Extending the hours may complicate the smooth recovery process used at Shouldice. More operating rooms are recommended.

4.

If the expansion decision is made on the basis of ROI ( Return On Investment), this is a very good investment.

(NPV is ignored, but can be added – no interest rate is given in the case.)

The expansion could be made on the other basis (i.e., Shouldice investors and personnel decide they are doing a good job and are happy with life, then the decision might well be made on other criteria.)