Specifications for 11m Ku-Band Full Motion Antenna Systems

| S/N | Item description | Specification | Compliance (Yes/No) | Offered Specifications |
| --- | --- | --- | --- | --- |
|  | Electrical and RF Specification |  |  |
| 1 | Operating Frequency Receive Tracking Transmit Ku Band | 10.70 to 12.25 GHz 10.70 to 12.25 GHz 12.75 GHz to 13.75 GHz |  |  |
| 2 | Antenna gain Receive at LNA input Transmit Ku band at FEED input | 60.0 dBi +20 log (f/10.70 GHz) 61.7 dBi +20 log (f/13.00GHz) |  |  |
| 3 | Feed Type | Multimode, Mono-pulse Tracking Feed having 4-port (2-Tx and 2-Rx ports orthogonal to each other) |  |  |
| 4 | Feed Insertion Loss | To be provided by the supplier |  |  |
| 5 | G/T at 5 deg. Elevation | 37.5 dB/K + 20 log (f/10.70GHz) (Break up analysis details of G/T shall be provided) |  |  |
| 6 | Antenna Side lobes | Better than the ITUR 580-6,First side lobe level better than 14 dB below main beam peak |  |  |
| 7 | Cross Polarization Isolation (Within 1 dB Beam width) Linear | ≥ 33 dB |  |  |
| 8 | Axial ratio Circular | 1.06 (0.51 dB) |  |  |
| 9 | Port to Port Isolation Transmit to Receive Transmit to Tracking Circular Receive to Receive Transmit to Transmit Linear Receive to Receive Transmit to Transmit | 100dB 100 dB 17 dB 17 dB 30 dB 30 dB |  |  |
| 10 | Transmit Port Power rating | 5 KW CW per Port |  |  |
| 11 | VSWR (Both transmit and receive ports) | 1.5:1 Typical |  |  |
| 12 | Wave guide Interface Tx. Ports Rx Ports | WR 75 WR 75 |  |  |
| 13 | Pressurization | Pressurized with dry air with in a range of 0.5 to 0.15 PSI. Duration over which pressure decreases from 0.5 to 0.15 PSI owing to leakage shall exceed 15 minutes. |  |  |
|  | Servo Specifications |  |  |
| 14 | Az / El Drive configuration Az El | Zero Backlash Motor Drives |  |  |
| 15 | Az / El Drive speeds | Max: ≥ 1 deg/sec, Min: 0.001 deg/sec |  |  |
| 16 | Azimuth and El acceleration | 10/sec2 min |  |  |
| 17 | Antenna control unit (ACU) Modes of operations | Standby, Rate mode, Memory Track, Autotrack (monopulse), Auto Phase, manual phase, Program Track, Step track, Built-in-Search, Preset Position, Star Track, Ephemeris Drive, Slew, Stow Lock, Single motor selection, Remote Computer Control, TLE Track, Autotrack over program drive ,option to feed offset angle to program drive mode |  |  |
| 18 | Primary Power supplies | 230 V ± 5% single phase, 400V ± 5% three phase, 50 Hz ± 2 Hz |  |  |
|  | Monopulse Tracking Specifications |  |  |
| 19 | Tracking | In LP and CP |  |  |
| 20 | Phasing | Manual and Auto phasing |  |  |
|  | Angular resolution – Az. & El. | 0.0010 |  |  |
| 21 | Polarization angular resolution | 0.10 |  |  |
| 22 | Az. / El Tracking speed (deg/sec) | Max: ≥ 1 deg/sec, Min: 0.001 deg/sec |  |  |
| 23 | Tracking Accuracy | Better than 1/10th of 3 dB Beam width (Break up analysis details shall be provided) |  |  |
| 24 | Pointing accuracy | Better than 1/5th of 3 dB Beam width (Break up analysis details shall be provided) |  |  |
| 25 | Beacon Tracking Dynamic range | > 65 dB |  |  |
| 26 | Acquisition range | ± 150 KHz with anti-side band rejection facility |  |  |
| 27 | Beacon carrier tracking threshold | Minimum C/KT of 45dBHz @ 1 kHz LBW |  |  |
| 28 | Tracking Beacon settability | 1 KHz step size |  |  |
| 29 | Frequency stability | 2 х 10-6 over 0 to 500 C with internal reference |  |  |
| 30 | Receiver PLL bandwidth | 100 Hz, 300 Hz, 1 KHz, 3 KHz (Typical) |  |  |
| 31 | Auto loop response for 3 dB error | Az: 0.6 sec rise time typical El: 0.6 sec rise time typical |  |  |
| 32 | Bore sight tracking null depth | 25 dB typical |  |  |
| 33 | System shall support single motor operation also in case of one motor failure. |  |  |
|  | Antenna Mechanical characteristics |  |  |
| 34 | Antenna size | About 11m diameter or more |  |  |
|  | Mount | Elevation over Azimuth |  |  |
|  | Optics | Shall be suggested by the supplier |  |  |
| 35 | Panel surface accuracy Main Reflector Sub reflector | < 0.5 mm (RMS). < 0.3 mm (RMS). |  |  |
| 36 | Azimuth Travel | ± 2700 |  |  |
| 37 | Elevation Travel | -1 to 910 |  |  |
| 38 | Polarization Travel in linear | ± 100 deg |  |  |
| 39 | Environmental |  |  |
| 40 | Wind Speeds | 80 KMPH Operational, 100 KMPH Gusting, 150 KMPH Survival (zenith) |  |  |
| 41 | Operational temperature | 00 to + 500 C |  |  |
| 42 | Relative humidity | 0 to 100% with condensation |  |  |
| 43 | Corrosion | Anti-corrosive, protective coating to all parts exposed to environment. |  |  |
| 44 | The tracking plate, tracking LNA, Tracking down-converter, Tracking Receiver, ACU, 1:2 LNA system (Ku-Band), Inject Couplers, etc., shall be the responsibility of the supplier |  |  |

Antenna and Feed System Safety

| Sl. No | Item description | Specification | Compliance (Yes/No) | Offered Specifications |
| --- | --- | --- | --- | --- |
| 1 | Limits and Display | Stow, Up pre-limit, Up final limit, Down Pre-limit, Down final limit, CW pre-limit, CW final limit, CCW Pre-limit, CCW Final limit, CW/CCW Zone change over, Low Elevation alarm switch. |  |  |
| 2 | End Stoppers | Mechanical stoppers at the final limit position for each axis of antenna rotation to withstand slew speed of antenna motion. |  |  |
| 3 | Hand held Portable Maintenance Unit | To be provided for manual movement during maintenance. One is required at ACU drive unit and one at antenna elevation platform. |  |  |
| 4 | Stow Lock Device | Stow lock devices in Az and El axis to mechanically arrest the antenna during hostile environmental conditions. |  |  |
| 5 | Auxiliary drive | Hand cranking facility for both the Az and El axis. |  |  |
| 6 | Emergency Stop Switches & Indication | Shall be deployed at all the critical antenna locations to inhibit the drive in the event of emergency. Viz., at Az Cone, at El platform, at ACU & in elevation hub. |  |  |
| 7 | Lightning Arrester | Lightning arrester assembly conforming to the latest safety standards to be provided for Antenna quadrapod and backup structure area. Earthing pits to be provided – 2Nos. |  |  |
| 8 | Cable wrap | Suitable arrangement to be provided for overcoming cable wraps. |  |  |
| 9 | Operator safety | Approach ladder with built-in safety measures to provide access to the El. Platform & Reflector surface. Safety railings around the azimuth cone and elevation platform. |  |  |
| 10 | Equipment lifting | Proper facility like motorized chain pulley or rope for lifting heavy equipment to the elevation platform to be provided. |  |  |
| 11 | Aviation lamp | Should be provided at appropriate locations with good visibility. |  |  |
| 12 | Seismic protection | Design should take care of seismic condition of site. |  |  |

| Sl. No | Item description | Compliance (Yes/No) | Offered Specifications |
| --- | --- | --- | --- |
|  | General Requirements |  |  |
| 1 | 1:2 LNA Ku-band Complex with remote controller for Ku-band frequencies (10.70 – 12.25 GHz) to be supplied. The output interface of both the bands and the carrier inject ports shall be N-type (female). 30 dB couplers to be incorporated before the LNA for carrier inject facility in all the feed ports. The minimum gain of the LNAs shall be 60 dB. |  |  |
| 2 | The Gain and G/T analysis breakup, Pointing and tracking accuracy analysis breakup to be provided along with the quote. |  |  |
| 3 | All sub-systems shall have serial or TCP/IP interface for remote monitor and control purposes. |  |  |
| 4 | All sub-systems shall have full-fledged Remote / Local control provision. |  |  |
| 5 | ACU shall have at least 02 Nos of serial or TCP/IP interface for MCS. |  |  |
| 6 | Remote shall mean control via MCS (Server & Client) and local shall mean control via the respective equipment front panel. However Feed switches control unit shall have local and remote units in addition to M & C port for computer interface. |  |  |
| 7 | Local / Remote selection shall be at the front panel of the respective local equipment. |  |  |
| 8 | Suitable racks to be supplied by the supplier to place supplier supplied equipments. |  |  |
| 9 | Supplier shall provide communication protocol for all the equipment for remote control through MCS. |  |  |
| 10 | MCS (software & hardware) will be the responsibility of MCF. |  |  |
| 11 | 2 Sets of operational and service manuals with maintenance (preventive and corrective) procedures and schedules to be provided for the supplied equipments. |  |  |
| 12 | The supplier shall organize the following major reviews during the project, to achieve better interaction and understanding with participation of MCF. |  |  |
|  | Preliminary Design Review (PDR): To review the soundness of the design specifications and to define the QA procedures, work plan and schedules. |  |  |
|  | Critical Design Review (CDR): To critically review, evaluate and finalize design aspects, firm up the details of equipment to be supplied and agree upon the subsequent test and evaluation procedures. |  |  |
|  | Operational Readiness Review (ORR): To review and evaluate the results of all tests on the systems vis a vis the specifications. |  |  |
| 13 | Supplier shall propose standard inspection practices and procedures, starting from raw materials to finished products. Joint inspection with MCF involvement, wherever necessary, shall be clearly specified. |  |  |
| 14 | As part of the “Factory Acceptance Tests” and “Site Acceptance Tests”, Supplier shall propose adequate tests and test-procedures which are acceptable to the ISRO in order to confirm the compliance to the specifications. |  |  |
| 15 | Supplier shall propose one set of critical spares required for 24X7 support with separate pricing. |  |  |
| 16 | Supplier shall involve MCF personnel during the installation, interfacing and testing of the systems. |  |  |
| 17 | Installation, Testing, commissioning and operational training to MCF personnel shall be the responsibility of the supplier. |  |  |
| 18 | The “factory acceptance testing” and the “site acceptance testing “ of the Feed, Antenna mechanical structure, ACU, antenna, Tracking receiver and the feed switching unit etc are to be conducted and will be witnessed by MCF Engineers. |  |  |
| 19 | Provision to be made for routing additional RF, control & power cables through the cable wrap at site during installation. |  |  |
|  | Support system The following needs to be provided by the supplier. |  |  |
|  | Civil |  |  |
| 20 | A finished built-up area of 25 Sq Mtrs with a height of 4 mtrs is to be provided for housing the HPAs, RF equipment, Antenna drive unit, ACU, Tracking Receiver, Electrical Distribution, etc. |  |  |
| 21 | The antenna is to be mounted on top of the above mentioned equipment building / pedestal. The Elevation axis shall have a clearance of about 13 mtrs from the ground level. |  |  |
| 22 | The equipment building / pedestal shall have a 2 mtr wide door to facilitate movement of equipment. |  |  |
| 23 | Required cut-outs to be provided in the equipment building / pedestal for Air-conditioning facilities. |  |  |
| 24 | The antenna foundation and load analysis breakup to be provided along with the quote |  |  |
| 25 | Required cut-outs to be provided in the equipment building / pedestal for HPA Exhaust. |  |  |
| 26 | The equipment building / pedestal shall have cable trenches / trays for routing RF, control and Power cables. |  |  |
| 27 | Provision to be made for routing the HPA output waveguide from the equipment building / pedestal to antenna hub. |  |  |
|  | Electrical |  |  |
| 28 | The equipment building / pedestal shall have required energy efficient electrical fittings for lighting, wall sockets for utility, electrical DB’s for UPS and utility separately, etc. |  |  |
| 29 | Customer responsibility is to provide one feeder point for short break (Utility Power) and one feeder point for Uninterruptible Power Supply (Technical Power). |  |  |
| 30 | Internal Distribution for the supplied equipment including Distribution Panels and Power Cables shall be the scope of the Supplier. |  |  |
| 31 | The equipment Building /Pedestal shall have the Lighting circuits with 30% from the Technical Power and remaining from the Utility Power. |  |  |
| 32 | The Lighting shall be designed such that the illumination levels in the area shall be suitable for Operation and Maintenance of the Equipments & as per relevant Indian and international Standards. The Design shall take care of light output at the end of life. |  |  |
| 33 | All switchgears shall be of Industrial standard only. |  |  |
| 34 | All the Cables & Wires should be ISI mark or International Standards. The insulation of Cables shall be FRLS OR HFFR type. |  |  |
| 35 | Additional points to be made available in the technical & utility power Distribution Panels for powering customer supplied equipments like Racks, HPAs, future augmentation, etc. |  |  |
|  | Safety |  |  |
| 36 | Required Grounding System for Antenna, Electrical DBs and RF Systems is to be designed and installed near the Building. The Supplier shall consider installing suitable connection points for antenna, RF and related equipments. |  |  |
| 37 | Lightning Protection System for Building as well as Antenna to be designed and installed by the supplier. |  |  |
| 38 | State of the art Analog Addressable Smoke / fire detection and alarm initiation system with Fire Alarm Control Panel to be installed. |  |  |
| 39 | First aid & fire fighting equipment to be deployed in and around the facility in sufficient number. |  |  |
| 40 | The building design shall take care of all safety aspects including human safety in the event of fire hazard or any calamity of similar nature. |  |  |
| 41 | The entry and exit to and from the station is to be regulated through an electronic access control system (supplied by customer); the door should be compatible for the above mentioned system. |  |  |
| 42 | Delivery Schedule The entire work involving Supply, Installation, Testing and Commissioning of the proposed antenna with civil structure is envisaged to be completed on TURN KEY basis, in about 24 months from the Effective Date of Contract (EDC). The supplier shall project best possible schedules with respect to fabrication, inspection, dispatch, installation, testing, commissioning, training and any other relevant matter related to the system, keeping in view the overall schedule indicated above. |  |  |