REQUEST FOR PROPOSAL

FOR

Establishing of 6 Tele-medicine nodes

May 2017

Development and Educational Communication Unit

Space Applications Centre

Ahmedabad-380015

1.0	Introduction:

As a part of Telemedicine project, ISRO has established more than 389 telemedicine (TM) nodes (306 Patient nodes + 66 Super Specialty (SS) nodes & 17 TM mobile nodes) across India including A&N region and Lakshadweep Islands. The satellite communication link hardware and software are provided by ViaSat Inc. USA. This network is using Client and Server based TM software and the TM server is placed at Telemedicine Hub at ISTRAC Bangalore. ISRO TM network has basically two types of TM nodes i.e.  patient nodes and SS nodes. TM software is provided by M/s Televital Bangalore.

The configuration of TM hub is 6.3m/400W Ext. C-band Telemedicine Hub (EDUSAT) located at “ISRO TELEMETRY TRACKING & COMMAND NETWORK (ISTRAC), Bangalore.  This Hub services the nationwide telemedicine network of the country and it is operational round the clock.

The network operates in Ext. C-band on GSAT-12 satellite and is configured in star topology. The OEM of Hub hardware & software is M/s ViaSat Inc. USA. Network is presently configured with one outbound carrier of 6Msps and 15 inbound carriers of 625 Ksps, which are accessed from remote stations in MFTDMA access scheme.

There is a need to establish 6 TM nodes at places

1. Jagannathpuri, Puri Odisha

2. Kedarnath Dham, Uttrakhand

3. Badrinath Dham, Uttrakhand

4. Rameshwaram, Tamil Nadu

5. Banaras Hindu University (BHU) Kashi (SS Node), UP

6. DGMS (Director General of Medical services) Army), New Delhi (SS Node)

The objective of this RFP is to get quotations to establish these TM nodes on turnkey basis.

2.0	ISRO TELEMEDICINE NODE CONFIGURATION:

The Tele-medicine nodes basically consists two elements 1. VSAT terminal 2. TM Hardware/software including diagnostic equipment/peripherals.

- List of Items for VSAT part of TM node:

- 1.8m solid dish antenna system including antenna base, feed boom, Ext. C - band feed, 2W BUC and PLL LNBC

- RG-6 IFL Cables set

- VSAT modem –RCST; Make –ViaSat, Model- LinkStar

- All required connecting cables and accessories for IDUs & ODUs

- ISRO TM network have two types of TM nodes as mentioned below:

- Super Specialist Node (SS node)

- Patient node (Fixed)

- Super Specialist Node (SS node)

- Multi Media PC, keyboard, mouse, speakers set and operating system with 24” (minimum) LED PC Monitor.

- SS node TM software- (will be provided by ISRO)

- USB based HD or better web camera

- Wired hand held microphone with XLR cable

- Multi-functional black and white laser printer

- 8 port LAN switch

- 2 KVA UPS with 2 Hrs. backup

- Miscellaneous items (power board, LAN Cables, etc.)

- Patient node (Fixed)

- Multi Media PC, keyboard, mouse, speakers set and operating system with minimum 24” LED PC Monitor

- Patient node TM software- (will be provided by ISRO)

- USB based HD Webcam or better

- Wired hand held microphone with XLR cable

- Vital track Multi-parameter device- Wi-Fi interface- with all the accessories

- Digital camera for radiology

- X-ray view box

- Oto-scope for ear diagnosis

- Derma-scope for skin diseases

- Digital stethoscope

- Multi-functional black and white laser printer

- 2 KVA UPS with 2 Hrs. backup

- 8 port LAN switch

- Miscellaneous items (LAN cable, power board, etc.)

3.0	Scope of work

Supply, integrate, install and commission of 6 TM nodes (2 Super Specialist and 4 patient nodes) on Turnkey basis. The following activities are to be carried out.

- Ext. C-band 1.8M Antenna systems with feed and mount, Ext. C-band 2W BUC, Ext. C-band PLL LNBC and VSAT modem (RCST) will be provided by DECU. These items are to be collected by the vendor from DECU/ISRO Ahmedabad.

- Vendor shall be required to confirm the site readiness prior to dispatch of items to the sites. Site address and contact person’s details will be provided by the DECU/ISRO at the time of placement of PO. Location/site address may change at the time of placing of PO.

- Vendor to supply the items of Patient /SS nodes as per list of deliverables mentioned in Annexure-I.

- Items supplied at Patient Node and Super specialist node should comply to the technical specifications given in Annexure-II.

- The Patient/SS node software shall be provided by DECU, ISRO and shall be installed and configured by TM software service provider.

- Vendor to test all the items provided by DECU at DECU/ISRO Ahmedabad, before dispatching to the respective site.

- After testing, these items are to be adequately packed for transportation to respective locations. (Transportation charges shall be paid at actuals on submission of bills/invoices). Vendor to obtain road permit in coordination with the user if required.

- Vendor to install and commission each TM node at the respective site as per the details provided and carryout functional test of each node in ISRO Telemedicine Network.

- Vendor shall make separate earthing pit by using suitable copper wire and Charcoal, salt, etc.

- Vendor shall be required to place adequate ballast weight on the antenna base, to keep stability of antenna even in high speed winds.

- Vendor shall be required to functional test each patient node with at least one Super Specialty (SS) node available in the ISRO TM network by uploading the patient history, diagnostic data to the server, referring the case to SS node, TM consultations through videoconference between SS and patient and also getting the SS prescription. Vendor shall also functional test the node with DECU/ISRO Ahmedabad.

- Vendor to hand over all the items of the TM node to site in-charge/custodian as per the format given in Annexure-III.

- Vendor to provide the operational and minor fault finding training to people deputed by the user like site coordinators/technicians which will include operational training of diagnostic equipment.

- Movement of manpower and material to be coordinated with DECU and respective site coordinators/user agency.

- Vendor to carry out Installation and Commissioning at site and submit the duly signed installation & commissioning certificate as per Annexure-IV to focal person at DECU Ahmedabad, without which payment shall not be released.

4.	Terms and Conditions

- It is a two-part tender. Vendor to submit the technical and commercial bid separately through Electronic Govt. Procurement System (EGPS).

- Vendor shall execute the activities as per the scope of work and submit I&C and handing and receiving certificates as per attached format.

- Vendor should have minimum one-year experience in the similar field. Vendor shall be required to submit the proof of experience like PO placed and the execution of the POs.

- Vendor shall submit the proof of capacity to execute the work within the time with trained man power.

- Vendor should plan the activity in coordination with ISRO TM hub and site coordinator/nodal officer of each node, contact details shall be provided by DECU/user agency.

- Vendor shall depute well trained engineer and technician for I&C of the sites, so that work is executed smoothly.

- The technical specification of all the equipment are mentioned as per attached Annexure- II.

- Vendor to clearly mention the make and model of each system/item.

- While complying, vendor to submit the data sheet/OEM compliance of each equipment, complying to the technical specifications. Any non-compliance to be mentioned clearly. Vendor may quote for better configuration system at par to our specifications. (price should be at par)

- Vendor’s personnel should carry one laptop, instant RF meter, required tools, spare cable and connectors, which shall be required during installation of TM node including optimization/re-orientation of antenna system.

- User agency and DECU, ISRO shall not be responsible for any injury or losses to vendor’s personnel deployed for I&C at the site.

- Vendor to provide the transit insurance for the material to be collected from DECU. ISRO Ahmedabad till the item is reached at respective site.

- Warranty: Vendor shall provide minimum 1-year onsite warranty support for all items supplied by them or as offered by the respective OEMs. Vendor to replace the faulty item under warranty. If original item is not available then, vendor to do a makeshift arrangement till the original item is received after repair.

- Towards assurance of performance of above services including warranty, vendor shall be required to submit the security in the form of Bank Guarantee (BG) equivalent to 10 % order value, which will act as security deposit (SD) as well as performance Bank Guarantee immediately after receiving the work the order. BG should be valid for the warranty period plus claim period of 2 months. The Bank Guarantee shall be returned within 30 days of after satisfactory execution of the contract.

5. 	Delivery Schedule:

Vendor shall be required to supply and install all TM nodes within 3 months from the date of acceptance of PO.

6.	Liquidated Damage (LD):

a.	In case of delay in execution of the work order beyond schedule mentioned above, liquidated damages at the rate 0.5% per calendar week of the value of work so delayed (one full node value shall be counted) shall be recovered from the vendor. Maximum amount of the LD recovered shall be limited to 10% of the value of the delayed portion.

b. 	Repair/Replacement of systems under warranty: All the systems (under warranty) is to be replaced by the vendor at site within 15 days from date of complaint lodged.

c.  	Downtime compensation (During warranty period): In the event of any system or station found to be non-operational after the formal complaint is registered with the vendor and if station (s) remain unattended beyond 15 working days without a valid reason, PBG will be invoked.

7.	Indemnity: By complying to this clause, Vendor indemnifies DECU, ISRO and against any action, claim or proceedings relating to infringement of all or any of the prevailing laws like workman’s Compensation Act 1923, Contract Labour (Regulation and Abolition) Act 1938, Industrial Disputes Act 1947, and Employee’s State Insurance Act 1952 during the currency of the order or any other act, not mentioned specifically.

8.	Arbitration:

In the event of any question, dispute or difference arising out of any terms and conditions of the order, the parties shall strive to find mutually acceptable solution, falling which, all questions, disputes or difference arising under or in connection with the order shall be settled through arbitration, (under Conciliation and Arbitration Act of India 1996) through Director, DECU. The award of the Arbitrator so appointed shall be final and binding on both the parties to this order.

9.	Compliance statement:

Vendor shall provide compliance statement for all the section/clause/points of RFP, including terms and conditions. Deviations if any shall be clearly explained/mentioned with effect on the performance of the system/TM node.

10.	Payment

Payment shall be released on pro-rata basis according to the work completed within 30 days of submission of claim to Accounts Officer (Bills), SAC with following documents:

- Signed Commercial invoice in original (in triplicate)

- Certificate of completion and acceptance issued by site in-charge (please refer annexure-IV)

- Vendor to submit bills/receipts, invoices & Challans of transportation charges at actuals.

- Certificate issued by DECU authorized representative for releasing payment.

Annexure-I

List of Deliverables and services to be provided:

| Sr. No | Item Description | Qty. | Unit Price in (Rs.) | Total price |
| --- | --- | --- | --- | --- |
| 1 | MM Computer with 24” LED Display monitor, Mouse, Keyboard, speakers set, compatible windows OS, etc. HP/Dell/HCL/ACER or equivalent |  |  |  |
| 2 | 8 port Ethernet switch make D-link/TP Link or equivalent. |  |  |  |
| 3 | USB based HD Webcam or better– I-ball/Logitech/or equivalent |  |  |  |
| 4 | Multi-Parameter monitor device which should support BP monitor, SPO2, ECG, thermometer, glucometer. Spirometer is optional. It should have all the accessories, leads and connectors to interface above device. Should have Wi-Fi Interface with the Patient node PC through Wi-Fi router |  |  |  |
| 5 | 12 lead ECG Machine with balloons, clamps and required connector and cables for online transfer of ECG (Optional) |  |  |  |
| 6 | Wi-Fi Router with four port of RJ-45 in-built in the router. Make- D-link/TP link or equivalent. |  |  |  |
| 7 | 16MP Digital camera with minimum 10X optical zoom. For scanning the X-ray Films. Sony/canon/Samsung or equivalent |  |  |  |
| 8 | X-ray View box (A3 Size) or bigger |  |  |  |
| 9 | Stethoscope with digital adapter for monitoring heart beats |  |  |  |
| 10 | Otoscope for examining ears with USB interface with patient node PC |  |  |  |
| 11 | Derma-Scope for skin with USB interface with TM PC |  |  |  |
| 12 | Wired Handheld microphone with phantom power supply and 10 Mtr XLR cable & XLR-EP converter of branded company like Bosh/Mipro, Ahuja or equivalent |  |  |  |
| 13 | Black and white multi-functional laser printer of branded company like HP/canon/Samsung or equivalent. |  |  |  |
| 14 | 2 KVA UPS with Hrs. backup batteries and High current charger. Make: Libert/APC/Emerson/or equivalent |  |  |  |
| 15 | High current charger compatible with supplied UPS |  |  |  |
| 16 | Earthing Kit with installation |  |  |  |
| 17 | Ballast weight for stability of antenna system minimum 12 in numbers (Approx. Size- 39x18.5x19 cm) and weight is around 10Kg. |  |  |  |
| 18 | Miscellaneous items (cables/connectors, Extension power boards, antenna ballast weights, etc. |  |  |  |
| 19 | Transportation Charges |  | At actuals |  |
| 20 | Installation and Commissioning charges per site |  |  |  |
| 21 |  |  |  |  |

Note: Quantity -6 of each item: 1.8m antenna system with mounting base, VSAT Modem make – ViaSat, Model – Linkstar, 2W Ext. C-band BUC and PLL LNBC will be given to vendor by DECU/ISRO, Ahmedabad.

Annexure-II

Technical Specifications of TM Peripherals

A.	TM Peripherals:

I.	Specialist & Patient nodes PC (with appropriate interfaces 	(Modules/Cards/Ports/Boxes/wireless etc.) for interfacing with diagnostic equipment.)

Technical Specifications (Equivalent or better):

- Processor			: Intel Core I5 4th Gen, 3.9 GHz, 6MB  cache, 1333MHz  FSB

    - Graphics 			: Intel® HD Graphics 4600

- Board/Chipset			: Compatible to the processor

- HDDs                 			: 1 TB of SATA, 7200 RPM

- RAM                   			: 4 GB DDR3 -1600

- Audio 				: on-board

- LAN (on board) 			: 100/1000 Mbps

- Monitor (Min.)   		: 24" Colour LED, Resolution 1024 X 768

- Dual Layer DVD Writer (16X or better) with 02 test media

- Keyboard & Optical Scroll Mouse

- Speakers			: Desktop Multimedia Amplispeakers

- Stereo Headphone with built-in Microphone combo with volume control

- Expansion Slots 			: 1 PCI Express and 1 PCI slots

- I/O ports and connectors	:  Preferably as following:

Front: Headphone, Microphone, 2 USB (2.0),

Rear: 2 USB (2.0), 2 USB (3.0), 1 standard serial port, PS/2 keyboard & mouse Other ports as required by diagnostic equipment.

- Operating System		: Windows 10

- Power				: 230 V ± 10%, 50Hz AC

II.	USB type Webcam Specification

| Sr. No. | Specifications | Detail |
| --- | --- | --- |
| 1 | Resolution | HD or better |
| 2 | Video Capture Speed | 25 fps@1080p or higher |
| 3 | Focus Type | Auto |
| 4 | Still Image Quality | 2 MP or higher |
| 5 | Low Light Correction | Automatic |
| 6 | Audio Noise Reduction | Automatic |
| 7 | Microphone Type | Dual stereo |
| 8 | OS compatibility | Must be compatible to PC supplied |
| 9 | Mounting Options | Clip based mounting to clip on monitor / LED TV |
| 10 | Accessories | All required accessories like mounting clip, software with lifetime license, cable etc. to be provided. |

III.	LAN Switch 	: 8 port 100/1000 Mbps Ethernet switch- D-link/TP-Link or equivalent

IV.	Wi-Fi Router: D-link/TP-Link or equivalent

| Sr. No. | Specifications | Details |
| --- | --- | --- |
| 1 | Device Interfaces | Four 10/100 LAN Ports ,One 10/100 WAN Port |
| 2 | Wireless Frequency Range | 2.4 GHz to 2.497 GHz |
| 3 | Antennas | Two fixed external Omni-directional antennas |
| Standards | IEEE 802.11b / IEEE 802.11g / IEEE 802.11n |
| 5 | Speed | 300 Mbps |
| Functionality |
| 6 | Security | WEP 64/128-bit data encryption WPS Wi-Fi Protected Access (WPA/WPA2) |
| 7 | Advanced | Web setup wizard |
| 8 | Firewall Features | Network Address Translation (NAT) Stateful Packet Inspection (SPI) MAC address filtering |
| 9 | Status LEDs | Power Internet status WLAN, LAN |

V.	Black and white multi-functions Laser printer:  it should meet the minimum requirement as given below;

Functions: Print, copy, scan

## Printing specifications

- Print speed: Normal: Up to 18 ppm or more
Print technology: Laser

- Print quality black (best): Up to 600 x 600 dpi (1200 dpi effective)

- Resolution technology: Fast Res 600; Fast Res 1200

- Print languages: Host-based

- Connectivity, standard: Hi-Speed USB 2.0 port

- Compatible operating systems; Windows 10

- Memory, standard: 8 MB or more

Paper handling

- Paper handling input, standard: 150-sheet input tray

- Paper handling output, standard: 100-sheet face-down bin

- Maximum output capacity (sheets): Up to 100 sheets

- Media sizes:  A4, A5, ISO B5, ISO C5, ISO C5/6, ISO C6, ISO DL

- Media types: Paper (plain, laser), envelopes, transparencies, labels, cardstock, postcards

Scanner specifications

- Scanner type:  Flatbed

- Scan file format: JPEG, TIF (compressed and uncompressed), PDF, GIF, BMP

- Scan resolution, optical:  Up to 1200 dpi

- Scan size, maximum: 216 x 297 mm

Digital sending standard features:

- Scan to E-mail

- scan to application

- scan to file

- File formats, supported: PDF, TIF, BMP,  GIF, JPG

Copier specifications

- Copy speed (normal) Black: Up to 18 cpm

- Copy resolution (black text):  Up to 600 x 400 dpi

- Copy resolution (color text and graphics): Up to 600 x 400 dpi

- Copy reduce / enlarge settings:  30 to 400%

- Copies, maximum:  Up to 99 copies

Power and operating requirements

- Power: 220 to 240 VAC (+/- 10%), 50/60 Hz (+/- 2 Hz)

- Operating humidity range: 10 to 80% RH

VI. 	Handheld Condenser Microphone with Phantom Power supply unit

| Sr. No. | Specification | Desired specifications | Compliance (Yes/No) | Remarks, if any |
| --- | --- | --- | --- | --- |
| 1 | Transducer type | Condenser |  |  |
| 2 | Polar pattern | Cardioid |  |  |
| 3 | Frequency response | 50Hz to 15 KHz |  |  |
| 4 | Sensitivity | ≥3mV/pa or ≥ -50dBV/pa |  |  |
| 5 | Output impedance | 100 to 300 Ohms |  |  |
| 6 | Connector | 3Pin XLR |  |  |
| 7 | Power supply | 48v phantom power |  |  |
| 8 | S/N Ratio | ≥64dB |  |  |
| 9 | Should be provide following cables: balanced XLR Male to XLR Female 10 meter XLR Female to 1/8”(3.5mm) mini plug -E.P connector - 2 meter (for connecting to PC Input). |  |  |
| 6.1 | Phantom power supply for Microphone |
| 1 | Input power | 12v/18v DC power supply |  |  |
| 2 | Output Phantom Power | 48V |  |  |
| 3 | No Of Channel | 1 |  |  |
| 4 | Input/output connector | XLR |  |  |
| 5 | Output level (both) Line and Mic available | Osprey – Line i/p Comp. - Mic i/p |  |  |
| 6 | AC Adaptor should be included. |  |  |
| 7 | ON/OFF Switch should be there |  |  |

VII.	2KVA UPS with 2 Hrs. backup and High current charger:

| SPECIFICATIONS | Details |
| --- | --- |
| Capacity | 2 KVA |
| Type | Processor controlled True Online, |
| Noise Level | Less than 50 dB |
| Operating Temperature | 0-50 degree centigrade |
| Humidity | 10 to 95% no-condensing |
| Harmonic Distortion | <2% (linear load) <3% (non-linear load) |
| Total DC bus voltage | 72 VDC or 48V DC or 36V |
| Battery recharge time |
| (After Complete discharge) to 100% charge | Approx. 8 Hours |
| Power Factor | 0.9 or better |
| Output Wave Form | Pure Sine wave |
| INPUT |
| Input | Single phase 3 wire |
| Input Voltage Range | 230VAC +/-5% |
| Input Frequency Range | 46-54Hz |
| OUTPUT |
| Output Voltage | 220/230/240 VAC programmable1 phase + N |
| Output Frequency | 50hz +/- 0.1%(Free running) |
| STATIC SWITCH | Should take care of 100% load transfer |
| (Bi-directional) for all ratings | without break |
| UPS SHUT DOWN |
| UPS shut down with alarm and Indication in case of |
| Output over voltage |
| Output under voltage |
| Battery Low |
| Inverter over load |
| Over temperature |
| BATTERY | Batteries current rating should be sufficient to provide 2 Hrs backup on full load. |

Technical Specifications of Diagnostic equipment:

- 12 lead ECG Machine: For live transfer of ECG

- 12 Lead ECG module: with 12 lead remote streaming –online

- Technical Specifications:

  - 10 patient cables with RFI filters, defibrillator protection

- patient isolation (both sequential and simultaneous type)

  - Freq. Response: 0.05 Hz to 125 Hz +/-3 dB

  - Leakage Current: < 10 micro amps

  - Input Impedance: >= 10 M ohms

  - Filters: HPF, LPF & Notch (50 Hz reject) or digitally

- programmable

  - A/D conversion: 12 bit (2.44 micro Volt resolution)

  - Sampling rate: 500 samples/sec

  - Sensitivity: 5,10,20 mm/mV

  - Dynamic Range: +/- 6 mV

  - Speed: 25/50 mm/sec

  - PC Interface: Serial and/or USB with cables

  - Software: OEM s/w with CD

  - Operation manual: English (In printed form)

  - Power requirement: 230 V, 50Hz ac (direct or with AC adapter)

- Make Model: Schiller, SAMVID or equivalent

- MULTIPARAMETER Monitor DEVICE

This single box should have following facilities along with the leads, connectors and cables to interface medical instruments.

| Sr. No. | Specification | Detail | Complied/ Not complied | Remarks |
| --- | --- | --- | --- | --- |
| 2.1 | ECG | Measurement range: ±0.5mVp ~ ±5mVp Heart Rate range: 20~300bpm Heart Rate accuracy: greater of ±2% or ±2bpm Alarm delay time: <=12s Input noise level for ECG amplifier: <= 30uVp-p Input impedance: >= 5M ohm (single ended) CMRR (common mode rejection ratio): >= 89dB ECG bandwidth: 0.5~40Hz (monitoring mode), 0.05~75Hz (diagnostic mode) |  |  |
| 2.2 | SpO2 | Measurement range: 35% ~ 99% Measurement accuracy: Arms <= 3% for SpO2 range from 70% ~ 100% Pulse Rate measurement: 30~240bpm ±2% or ±2bpm Update rate: 8 pulse beats Low perfusion performance: Accuracy of SpO2 & PR remains within specified range while pulse amplitude modulation ratio is as low as 0.4% |  |  |
| 2.3 | Noninvasive Blood Pressure | Pneumatic pressure measurement: 0~300mmHg with ±3mmHg accuracy Air leakage: <2mmHg/minute @ 300mmHg with 500cc cuff volume Systolic pressure range: 40~270mmHg for adult, 40~200mmHg for pediatric Diastolic pressure range: 10~210mmHg for adult, 10~150mmHg for pediatric MAP range: 20~230mmHg for adult, 20~165mmHg for pediatric BP accuracy: mean error <= ±5mmHg with standard deviation <= 8mmHg. Pulse Rate measurement: 40~240bpm with 2% or ±2bpm accuracy Blood pressure measuring time: < 30sec for typical adult (80/120mmHg, 75bpm) at manual or auto mode Time interval selection at auto mode: 1, 2, 3, 4, 5, 10, 15, 30, 60, 90 minutes. Over-pressure protection with limit of 320±10mmHg by dual transducers. |  |  |
| 2.4 | Respiration | Measurement range: 0~120rpm Measurement accuracy: ±10% |  |  |
| 2.5 | Temperature | Measurement range: 25.0~45.0 °C Measurement accuracy: ±0.2 °C Response time: <= 30sec |  |  |
| 2.6 | Blood Sugar | Measurement range: 20~600 ml/dl Blood sample requirement: 0.7μL Used strip detection Response time < 10sec |  |  |
| 2.7 | Body Weight | Measurement range: 5~180kg BMI calculations Measurement in Lbs and Kgs Bluetooth enabled |  |  |
| 2.8 | Communication Support | 3G/GPRS packet data Wi-Fi (802.11 a/b/g) |  |  |

3.	Digital Camera:

  - 16 Megapixels above

  - Optical Zoom: 10x above

  - with 3.0-inch LCD or bigger

  - Manual and auto focus

  - USB interface to connect with PC

  - 16 GB Memory card

  - Lithium Battery

  - Battery Charger

4.	X-ray View Box:

Should have the following features;

- Light source: LEDs

- It should not have UV Emissions and high heat generation

- Digital dimmer technology with minimum 12 steps to get the perfect brightness.

- It should be light and slim

- Reliable magnetic nipper

- Over 95% uniformity in light across the screen

- Film activated switch / film sensor - automatic shutdown if no film inside for 2 sec

- Should have 9300k white and light-blue color temperature which is ideally suitable for viewing X Ray.

5.	Otoscope

- TRUE 1.3 Megapixel resolution

- 150x digital magnification

- 50x optical magnification

- Resolution: 720x480

- Formats: YUY2, AVI

6.	Derma-Scope

- Sensor Resolution: 2.0M pixels.

- Still Image Resolution: 1600x1200 pixels (Format: BMP).

- Video Resolution: 1600x1200 pixels (Formats: MJPG, YUY2,

- Frame Rate: 30FPS)

- Magnification: 15x - 50x (Native Optical), 15x - 150x (Digital).

- Lens Assembly: Dual Lenses, 3-Layer Glass, 650nm cutoff,

- Integrated Polarizer with 12 settings.

- Lighting: 8 Ultra-Bright LEDs with fully adjustable brightness.

- Interface: USB2.0 (USB Cable Length: 180cm). Built-in snapshot button. Rugged industrialized construction.

- Software: Scalable Window, Zoom, Freeze, Resolution, Rotate,

Flip, Region of Interest (ROI), Real time measurements,

- Automatic/Manual white balance

Note: All the diagnostic equipment should be compatible to the existing TM software Vitalware Ver. 4.0. The software is provided by M/s Televital Pvt. Ltd. Bangalore.  It is required that vendor should sufficient experience to interface this equipment to the software and provide the training to users. Otherwise vendor to provide a letter for technical support during warranty period from M/s Televital Pvt. Ltd.

Annexure - III

# TM Node Items handing/Taking over Certificate

| Sr. No. | Item Description | Information to be filled |
| --- | --- | --- |
| 1 | ISRO PO Reference |  |
| 2 | Name of state |  |
| 3 | Location & address of the TM node |  |
| 4 | Name of the TM site-in-charge/local custodian |  |
|  | (a) Telephone (O) |  | (b) Fax (O) |  |
|  | (c) Mobile |  | (d) E-mail ID |  |
| 5 | Site Visit Date |  |
| Antenna and IDU / RCST |
| Sr. No. | Description | Make / Model No. / Sr. No. (If available) | Functional Status | Remarks |
| 1 | 1.8 m Ext C Band Antenna with feed and mount |  | Working / Not Working |  |
| 2 | Ext-C band PLL LNBC |  | Working / Not Working |  |
| 3 | 2W Ext-C Band BUC |  | Working / Not Working |  |
| 4 | IFL Cables set of 2 cables |  | Working / Not Working |  |
| 5 | IDU / RCST | ViaSat, Linkstar | Working / Not Working |  |
| 6 | RCST Power Adaptor for RCST |  | Working / Not Working |  |
| 2 KVA UPS WITH 2Hrs. Backup and high current charger |
| 1 | Batteries |  | Working / Not Working |  |
| 2 | 2 KVA UPS with 2 Hrs backup |  | Working / Not Working |  |
| 3 | Additional high current charger (Built in with Battery Cabinet) |  | Working / Not Working |  |
| TM Node Peripherals and Diagnostic Equipment’s |
| Sr. No. | Description | Make / Model No. / Sr. No. (If available) | Functional Status | Remarks |
| 1 | Multi Media PC with graphics card, keyboard, mouse, speakers set and operating system with 24” LED PC Monitor |  | Working / Not Working |  |
| 2 | Patient node TM software- (will be provided by ISRO) |  | Working / Not Working |  |
| 3 | USB based Webcam with minimum resolution HD |  | Working / Not Working |  |
| 4 | Multi-parameter device- WiFi interface- with all the accessories |  | Working / Not Working |  |
| 5 | Digital camera for radiology |  | Working / Not Working |  |
| 6 | A3 Size X-ray view box |  | Working / Not Working |  |
| 7 | Stethoscope with Digital Adapter |  | Working / Not Working |  |
| 8 | Otoscope for ear diagnosis |  | Working / Not Working |  |
| 9 | Derma-scope for skin diseases |  | Working / Not Working |  |
| 10 | Black and white multi-functional laser printer |  | Working / Not Working |  |
| 11 | 12 lead ECG machine (optional) |  | Working / Not Working |  |
| 12 | 8 port LAN switch |  | Working / Not Working |  |
| 13 | Wi-Fi Router |  | Working / Not Working |  |
| 14 | Wired HH microphone with phantom PSU |  | Working / Not Working |  |
| 15 | Earthing |  | Working / Not Working |  |
| 16 | Miscellaneous items (cable/connector, power board, remote cells, etc. |  | Working / Not Working |  |
| Remarks/Any additional information if any: |
| HANDED OVER BY: Signature of the Vendor's Engineer | RECEIVED BY: Signature of the site in-charge/Local custodian |
| Name: | Name: |
| Designation: | Designation: |
| Contact details: | Contact details |
| Date: | Date: |

# Annexure-IV

# Certificate of Installation and commissioning of Telemedicine Node:

| Sr. No. | Item Description | Information to be filled |
| --- | --- | --- |
| 1 | ISRO PO Reference |  |
| 2 | Name of state |  |
| 3 | Location & address of the TM node |  |
| 4 | Name of the TM site-in-charge/local custodian |  |
|  | (a) Telephone (O) |  | (b) Fax (O) |  |
|  | (c) Mobile |  | (d) E-mail ID |  |
| 5 | Site Visit Date |  |
| Antenna and IDU / RCST |
| Sr. No. | Description | Make / Model No. / Sr. No. (If available) | Functional Status | Remarks |
| 1 | 1.8 m Ext C Band Antenna with feed and mount |  | Working / Not Working |  |
| 2 | Ext-C band PLL LNBC |  | Working / Not Working |  |
| 3 | 2W Ext-C Band BUC |  | Working / Not Working |  |
| 4 | IFL Cables set of 2 cables |  | Working / Not Working |  |
| 5 | IDU / RCST | ViaSat, Linkstar | Working / Not Working |  |
| 6 | RCST Power Adaptor for RCST |  | Working / Not Working |  |
| 2 KVA UPS WITH 2Hrs. Backup and high current charger |
| 1 | Batteries |  | Working / Not Working |  |
| 2 | 2 KVA UPS with 2 Hrs backup |  | Working / Not Working |  |
| 3 | Additional high current charger (Built in with Battery Cabinet) |  | Working / Not Working |  |
| TM Node Peripherals and Diagnostic Equipment’s |
| Sr. No. | Description | Make / Model No. / Sr. No. (If available) | Functional Status | Remarks |
| 1 | Multi Media PC with graphics card, keyboard, mouse, speakers set and operating system with 24” LED PC Monitor |  | Working / Not Working |  |
| 2 | Patient node TM software- (will be provided by ISRO) |  | Working / Not Working |  |
| 3 | USB based Webcam with minimum resolution HD |  | Working / Not Working |  |
| 4 | Multi-parameter device- WiFi interface- with all the accessories |  | Working / Not Working |  |
| 5 | Digital camera for radiology |  | Working / Not Working |  |
| 6 | A3 Size X-ray view box |  | Working / Not Working |  |
| 7 | Stethoscope with Digital Adapter |  | Working / Not Working |  |
| 8 | Otoscope for ear diagnosis |  | Working / Not Working |  |
| 9 | Derma-scope for skin diseases |  | Working / Not Working |  |
| 10 | Black and white multi-functional laser printer |  | Working / Not Working |  |
| 11 | 12 lead ECG machine (optional) |  | Working / Not Working |  |
| 12 | 8 port LAN switch |  | Working / Not Working |  |
| 13 | Wi-Fi Router |  | Working / Not Working |  |
| 14 | Wired HH microphone with phantom PSU |  | Working / Not Working |  |
| 15 | Earthing |  | Working / Not Working |  |
| 16 | Miscellaneous items (cable/connector, power board, remote cells, etc. |  | Working / Not Working |  |
| Sr. No | Parameter | Specification | Measured value/Remarks |
| 1 | BER for inbound carrier | ≤ 0.00020 |  |
| 2 | Ping test | Ok / Not OK |  |
| 3 | Image/data transfer performance | Ok / Not OK |  |
| 4 | Video performance | Ok / Not OK |  |
| 5 | Audio performance | Ok / Not OK |  |
| 6 | UPS (mains <–> battery switching) | Ok / Not OK |  |
| 7 | Line to Neutral Voltage | 230 V ± 10% |  |
| 8 | Neutral to Earth Voltage | ≤ 5V |  |

Any Other Information/Remarks:

Above mentioned items are supplied and successfully installed and commissioned at the site. Site is operational.

Signature of Vendor/Engineer				Signature (With Stamp) of TM site-in-charge/

local Custodian

Name & Designation:					Name & Designation:

Date:							Date: