OPERATING & INSTRUCTIONS MANUAL S230 12V/DC (24V OPTION) REV.1

FULL GUAGE CONTROLLER MODEL: MT512E 2HP Vers.12

- 12V/DC OPERATION

- 24V/DC OPTION WITH CHANGES TO ELECTRICAL COMPONENT CONNECTIONS

- NOTE:

- THESE INSTRUCTIONS APPLY TO THE S230 (12V/DC - 220V/AC) DUAL TEMPERATURE FREEZER

- WHEN 220V/AC SUPPLY IS USED, PLEASE ENSURE THAT THE 12V/DC CONECTION IS DISCONECTED.

IMPORTANT: REMEMBER TO COMPLETE THE WARRANTY CARD AND RETURN IT TO THE ADDRESS BELOW.  FAILURE TO DO SO MAY LEAD TO DIFFICULTY IN PROCESSING WARRANTY CLAIMS.

MINUS 40 12VOLT REFRIGERATORS AND FREEZERS

PRODUCT			STORAGE TIME		TEMPERATURE

Uncooked meat,			1 - 2 days		8 to 10 °C

Milk, cheese,			3 - 4 days		5 to 8 °C

Vegetables, etc.			7 days +			9 to 5 °C

Frozen meat, Poultry		up to 	7 days		-6 to -2 °C

Vegetables and 			up to 14 days		-8 to -4 °C

Pre-prepared foods		not more than 30 days 	-15 to -12 °C

- 12 VOLT OPERATION

- The battery used will of course require re-charging periodically.

- This can be done using a charger operating from the mains, by using a vehicles electrical system or by means of solar panels.

- For these units the recommended minimum battery capacity is 100 amp hours.

- This size battery will operate the unit continuously for approximately 17 hours without re-charging.

- This model Freezer (S230 Dual Temperature freezer), can also operate on 24V/DC electrical current.

- In order for this freezer to operate on 24V/DC, changes need to be made to the electrical connections on the Digital Temperature Controller.

PLEASE CONSULT WITH THE MANUFACTURER BEFORE MAKING THE CHANGES FROM 12V/DC TO 24V/DC.

- Currently, the electrical supply to the temperature controller is connected in the 12V/DC position.

- When 24V/DC power is being used, the connections MUST BE REMOVED FROM THE 12V/DC CONNECTOR POSITION AND RECONNECTED TO THE 24V/DC POSITION AS INDICATED ON THE TEMPERATURE CONTROLLER

WIRE LENGTH UP TO:	*WIRE X-SECTION - AREA SQUARE MM

2, 5M			 2, 5

4, 0M			 4, 0

6, 0M			 6, 0

10, 0M			 10, 0

16, 0M			 16, 0

- FOR USE WITH SOLAR PANELS

The supplier of the solar power system should be consulted to determine whether additional batteries or photovoltaic panels are required.

Contact Minus 40 for details of Solar Panel kits selected specially for each refrigerator/freezer model.

# PARAMETER TABLE & SETTINGS FOR FULL GUAGE CONTROLLER MODEL: MT512E 2HP Vers.12

Control Temperature Adjustments (SET POINT)

Press SET for 2 sec. until appears SET, and release it after that.

The adjusted operation temperature will appear. Use UP & DOWN arrow to change value and then press SET to record it.

# 1	SET POINT:	3.5°C

| 2) | PARAMETER TABLE | NTC |  |
| --- | --- | --- | --- |
| FUN | Description | Values | Unit |
| F01 | Access code:123 (one hundred & twenty three) | - | - |
| F02 | Set point | 3.5 | °C |
| F03 | Indication Offset | 0 | °C |
| F04 | Minimum set point allowed to the end user | -15 | °C |
| F05 | Maximum set point allowed to the end user | 10 | °C |
| F06 | Control differential (hysteresis) | 3 | °C |
| F07 | Operating mode | 0 | - |
| F08 | Minimum output time on | 60 | Sec |
| F09 | Minimum output time off | 60 | Sec |
| F10 | Cooling time | 0 | Min |
| F11 | Defrost Time (*) | NO | Min |
| F12 | Initial state up on energizing the instrument | 0 | - |
| F13 | Indication of the temperature locked during defrost (**) | NO | - |
| F14 | Instrument energization delay | NO | - |
| F15 | Additional time at the end of first cycle | NO | Min |
| F16 | Situation of the compressor with the damaged sensor | 0 | °C |
| F17 | Compressor time on in case of error | 2 | Min |
| F18 | Compressor time off in case of error | 2 | Min |
| F19 | Intensity of the digital filter (***) | NO | - |
| F20 | Time for function lockdown | NO | - |
| F21 | Control function lockdown | NO | - |

Parameters configuration

- Access the function F01 by pressing at the same time DOWN and UP for 2 sec. until appear Fun releasing then after that. Soon will appear F01. and then press SET (short touch).

# Use DOWN and UP to enter the access code (123), and then press SET

- Select the desired function and visualize the configured value

- Use DOWN and UP to change the value and then press SET to record the configured value and return to the functions menu.

- To reset the menu and return to normal operation (temperature indication), press SET until appear ---