1-01.2.GR1

Abbreviations

1-01.2(2).GR1

Items of Work and Units of Measurement

1-01.2(2).INST1.ITS.DT1

Section 1-01.2(2) is supplemented with the following:

1-01.2(2).OPT1.ITS.DT1

(NWR ITS March 5, 2012)

bps	Bits Per Second of Serial Data

CCTV	Closed Circuit Television

CC	Camera Cabinet

CPU	Central Processing Unit

CWDM	Course Wave Division Multiplex

dB	Decibel

dBm	Decibel referenced to 1 milliwatt

DS	Data Station

DS-1	Digital Signal Level 1 (1.544 Mbits/s)

DS-3	Digital Signal Level 3 (44.736 Mbits/s)

ES	Electronic Surveillance

EPROM	Electronically Programmable Read-Only Memory

FM	Frequency Modulation

HAR	Highway Advisory Radio

HARS	Highway Advisory Radio Sign

HART	Highway Advisory Radio Transmitter

ITS	Intelligent Transportation System

Kbps	Thousands of Bits Per Second of Serial Data

LASER	Light Amplification by Stimulated Emission of Radiation

LED	Light Emitting Diode

Mbps	Millions of Bits Per Second of Serial Data

MMFO	Multimode Fiber Optics

MUX	Multiplexer

nm	Nanometer (10-9 meter)

OC-1	Optical Carrier Level 1 (50.84 Mbits/s)

OC-48	Optical Carrier Level 48 (2.44 Gbits/s)

OFNR	Optical Fiber Nonconductive Riser

OSP	Outside Plant

OTDR	Optical Time Domain Reflectometer

PTZ	Pan, Tilt, Zoom (for camera control)

RGB	Red, Green, Blue video signals

RMU	Rack Mounting Unit (1.75 inches)

SC&DI	Surveillance, Control and Driver Information

SMFO	Singlemode fiber optics

SONET	Synchronous Optical Network

STS-1	Synchronous Transport Signal Level 1 (electrical 50.84 Mbits/s)

T1	See DS-1

T3	See DS-3

TC	Terminal Cabinet

TMS	Traffic Management System

TMC	Traffic Management Center

TWP	Twisted Wire Pair

UPS	Uninterruptible Power Supply

VMS	Variable Message Sign

WSTA	Weather Station

ZIF	Zero-Insertion Force

1-08.9.GR1

Liquidated Damages

1-08.9.INST1.GR1

Section 1-08.9 is supplemented with the following:

1-08.9.OPT2.docx

(******)

Unplanned disruptions to the Intelligent Transportation System (ITS) will result in impacts to the traveling public, increase fuel consumption, vehicle operating costs, pollution, and other inconveniences and harm.

Accordingly, the Contractor agrees:

1.	To pay $250.00 liquidated damages per 15 minutes for each 15 minute period that the Contractor fails to restore the proper operation of an existing ITS element following an unplanned disruption as specified in the subsection Existing System Disruption and Restoration of the Special Provision Illumination, Traffic Signal Systems, Intelligent Transportation Systems,  and Electrical.

2.	To authorize the Engineer to deduct these liquidated damages from any money due or coming to the Contractor.

8-20.GR8

Illumination, Traffic Signal Systems, Intelligent Transportation Systems, and Electrical

8-20.1.GR8

Description

8-20.1.INST1.ITS.DT1

Section 8-20.1 is supplemented with the following:

8-20.1.OPT1.ITS.docx

(******)

INTELLIGENT TRANSPORTATION SYSTEM (ITS)

3a.  Traffic Data Accumulation and Ramp Metering System

3b.	Closed Circuit Television System

3c.  Variable Message Sign System

3d.		Active Traffic Management System

3e.	Communication Conduit System

3f.	Communication Cables and Interfaces

3g.	Video, Voice & Data Distribution and Transmission System

8-20.1.OPT2.ITS.docx

(******)

Traffic Data Accumulation And Ramp Metering System

This work shall consist of furnishing, installing, and testing all materials and equipment necessary to provide a complete in place the traffic data accumulation and ramp metering system and when specified, the modification of such existing systems.

8-20.1.OPT3.ITS.DT1

(******)

Closed Circuit Television System

This work shall consist of furnishing, installing, and testing all materials and equipment necessary to provide a complete and operable extension to the existing closed circuit television (CCTV) system.

8-20.1.OPT4.ITS.DT1

(NWR ITS February 11, 2002)

Variable Message Sign (VMS)

This work shall consist of furnishing, installing and testing all materials and equipment necessary to complete in place the variable message sign system, and when specified, the modification of such an existing system.

8-20.1.OPT5.ITS.DT1

(NWR ITS February 11, 2002)

Highway Advisory Radio (HAR) System

This work shall consist of the following:

*** $$1$$ ***

8-20.1.OPT5(A).ITS.DT1

(NWR ITS October 16, 2006)

Highway Advisory Radio Transmitter (HART)

The Contractor shall furnish all labor, materials, tools, equipment and services for the installation of a fully operational Highway Advisory Radio Transmitter (HART) as intended by the Special Provisions and Plans.  The HART shall include, but not be limited to: electronics rack, amplitude modulated transmitter, power supply, voice storage unit, digital communications module, equipment cabinet, antenna, pole, conduits, conductors, junction boxes, and power and communication services.

The Contractor shall provide and install the HART as shown in the Plans.  The HART will be controlled remotely from the Traffic Management Center (TMC) at Dayton Ave. in Shoreline by the use of Contracting Agency-owned communication lines.

8-20.1.OPT5(B).ITS.DT1

(NWR ITS February 23, 2009)

Highway Advisory Radio Sign (HARS)

This work shall consist of furnishing, installing and testing of new sign and beacons, sign control equipment and cabinet, and other equipment necessary to provide for an operational highway advisory radio system as specified in these Special Provisions.

8-20.1.OPT6.ITS.docx

(******)

Active Traffic Management (ATM) System

This work shall consist of furnishing, installing, and testing new lane control signs, side-mount dynamic message signs, variable message signs, mounting brackets, sign controllers, ATM cabinets and all materials and equipment necessary at location identified on the Plan to complete in place the active traffic management system, and when specified, the modification of such an existing system.

8-20.1.OPT8.ITS.DT1

(NWR ITS February 11, 2002)

Communication Conduit System

This work shall consist of furnishing and installing the facilities used to mechanically accommodate the communication components of the ITS System.  The Contractor shall be responsible for interfacing with the existing communications system and satisfying system compatibility with regard to the existing facilities and this communications system extension.  Conduit shall be supplied as a system from a single manufacturer providing all of the steel and PVC conduit; all required fittings, terminations, and other installation accessories; all in accordance with the Plans, the Standard Specifications and these Special Provisions.

8-20.1.OPT9.ITS.DT1

(NWR ITS February 11, 2002)

Communication Cables And Interfaces

This work shall consist of furnishing, installing and testing all materials and equipment necessary to complete in place the communication cable and interface system and, when specified, the modification of such an existing system.

8-20.1.OPT10.ITS.DT1

(NWR ITS February 11, 2002)

Video, Voice, & Data Distribution And Transmission Systems

This work shall consist of furnishing and installing all materials and equipment necessary to complete in place the video, voice, and data distribution and video transmission systems, and when specified, the modification of such existing systems.

8-20.1.OPT11.ITS.DT1

(NWR ITS February 23, 2009)

Communication Hub / Concrete Universal Enclosure (CUE)

This work shall consist of providing and installing a concrete universal enclosure (CUE), mechanical and environmental system to support the requirements of the housed equipment in four 19-inch rack frames, two 23-inch rack frames (6.9 feet in height).

8-20.2.GR8

Materials

8-20.2.INST1.ITS.DT1

Section 8-20.2 is supplemented with the following:

8-20.2.OPT2.ITS.DT1

Closed Circuit Television System

8-20.2.OPT2(A).ITS.docx

(******)

Video Camera Assembly

Video cameras shall be supplied as a unit including camera with integrated lens, id generator, camera controller, video encoder, pressurized environmental enclosure, pan and tilt mechanism, faceplate wiper and rain/sun shade.  Each video camera shall be provided with a camera control cable, IP67 RJ45 coupler, PoE++ (Power-over-Ethernet++) injector and PoE++ surge protector.  Camera mounts shall be provided as identified in the plans.  The camera assembly shall be a RISE 4260HD series camera positioning system, manufactured by CohuHD.

1.	Equipment Model Numbers:

RISE camera system:		Model 4261-1100

PoE++ Injector:		Model 7412007-003

PoE++ Surge Protector		Model 7412009-001

IP67 RJ45 Coupler		Model 7610203-001

Video camera control cable	Model CA276A-XXX (XXX = length in ft)

Camera Mounts:

Side pole mount:	Model 8185-4

Wall mount:		Model 8425-7

Pedestal:	Model 7411542-001

2.	Manufacturer Information:

CohuHD Costar

7330 Trade St

San Diego, CA  92121

Telephone:  (858) 391-1800

www.cohuhd.com

8-20.2.OPT2(C).ITS.DT1

(NWR ITS February 23, 2009)

Existing Camera Pole(s)

When modifying an existing camera pole that currently has a heavy-duty pan/tilt unit and 8200 series camera mounted on it, the Contractor shall perform the following tasks:

- Modify the top of the pole by cutting a 1.75-inch diameter hole in the center of the mounting plate for the camera control cable to pass through into the top section of the pole.   Paint the mounting plate with cold galvanizing paint to repair the finish damaged by drilling and cutting.

- Install a short pedestal mount (Pelco PM2010) on the modified base plate.

- Remove the existing pole-mounted junction box and cap the remaining holes.

- Install new camera and cable in accordance with the details.

8-20.2.OPT2(D).ITS.docx

(******)

Camera Control Cabinet (Pad Mount)

The cabinet shall meet the requirements of section 9-29.13(12) ITS Cabinet.

Section 9-29.13(12) is supplemented with the following:

1.	One controller unit shelf, which attaches to the front and back rails of the EIA rack, shall be provided. The shelf shall be fabricated from aluminum and shall contain a roll-out flip-top drawer for storage of wiring diagrams and manuals.

2.	Each camera control cabinet shall house one termination block for the termination of each camera control cable.  Camera control cables shall be identified and marked by the Contractor.

8-20.2.OPT2(E).ITS.docx

(******)

Camera Control Cabinet (Pole Mount)

Camera control cabinets shall contain the equipment shown in the Plans.  The cabinet shall have the same features as the pad-mounted version except the dimensions shall be 36 inches high, 24 inches wide and 18 inches deep and include a single door.  The cabinet and door shall meet the same requirements as the pad-mounted version.  The cabinet shall include the following:

1.	Cabinets shall be fabricated of 0.125” sheet aluminum, 5052 alloy, with mill finish, in accordance with Section 9-29.13(7)D, Item number 1.  Painted or anodized aluminum is not allowed.

2.	Cabinet doors shall have a three-point latch and two-position stop assembly with spring loaded construction core lock capable of accepting a Best Lock Company 6-pin CX series core. The Contractor shall supply green construction cores. Upon contract completion, the Contractor shall deliver two master keys and one core removal key to the Engineer.

3.	The cabinet shall be equipped with a rack-mounted power distribution assembly (PDA).  The PDA shall contain one duplex 120 VAC power receptacle for each camera and a main circuit breaker (120 VAC, 15 amp).  The ground bus, neutral bus, surge suppresser and filter unit, (120 VAC, 50 amp) and all other power distribution components shall be mounted in, or on, the PDA or side panel as shown in the plans such that they are readily accessible, provide dead front safety, and all hazardous voltage points are covered to prevent inadvertent contact.

4.	Each camera control cabinet shall house one termination block for the termination of the camera control cable.

5.	The Contractor shall provide and install a rack-mounted fiber optic patch panel as shown in the Plans and as specified elsewhere in these Provisions.

6.	The cabinet shall include a standard EIA 19-inch (ANSI/EIA RS-310-C) rack for mounting equipment.

8-20.2.OPT8.ITS.DT1

Variable Message Sign (VMS)

8-20.2.OPT8(A).ITS.docx

(******)

Variable Message Sign Assembly

The variable message signs and controllers shall be supplied by the following vendor:

Daktronics, Inc.

321 Daktronics Dr.

Brookings, SD 57006-5128

Tel: (800) DAKTRONICS

Fax: (605) 697-4300

Email: sales@daktronics.com

VMS Sign Display

The following is a list of part numbers that shall be used for the variable  message signs for this project, if the vendor has a newer product at the time of construction which supersedes these part numbers, the newer product shall be considered if it meets all the same standards:

1.	Equipment Model Numbers:

Side-Mount Dynamic Message Signs:               VF-2420-80x80-20-RGB

Lane Control Signs:                                           VX-2420-64x64-20-RGB

Walk-in Access Variable Message Signs:          VF-2020-54x150-34-RGB

VF-2020-96x336-20-RGB

Front Access Variable Message Signs:             	VF2420-96x256-20-RGB

VF2420-96x336-20-RGB

Dedicated DMS	VM-1020-7x50-66-RG-TRICOLOR/2 panels

All variable message signs shall operate on 120/240V power.

VMS Sign Beacon

Three flashing beacons shall be installed on top of the sign housing.  The beacons shall be as specified in Section 9-29.21.  The 12 inch lamps shall be LED type, amber in color and meet the applicable portions of Section 9-29.16(2)A.

The beacons shall be aluminum and consist of single section, 12 inch traffic signal heads with cadet visor, square doors, and amber display.  The center beacon shall flash alternatively to the two outside beacons.

Controllers for flashing beacons shall be as specified in Section 9-29.15, with aluminum sheet metal cabinets. The sign controller shall operate the beacons as commanded by the NTCIP communications protocol.

Sign Mounting Hardware

A VMS, sign structure, foundation, and a maintenance walkway are included in the construction.  The sign housing shall be provided with all necessary hardware including sign mounting beams, vertical and horizontal brackets, maintenance walkways, and all related hardware to install the VMS.

The walkway shall be level with the bottom edge of the VMS.  All mounting hardware shall conform to the G series Standard Plans, the Standard Specifications and the Plans.  All nuts used in the mounting hardware shall be self-locking nuts with nylon inserts. VMS’s shall be attached or mounted to sign structures by means of positive connections - defined as through-bolted connections.  The use of clips or clamps to accomplish the attachment or mounting of such signs and assemblies is prohibited.

The VMS housing, structural framing, face covering, and mounting members shall be designed to withstand a wind velocity of 100 mph with a 30 percent gust factor and shall otherwise comply with the latest requirements of AASHTO’s Standard Specifications for Structural Supports for Highway Signs, Luminaires and Traffic Signals.

Control System

The VMS control system shall include all excavation, backfill, conduit, wiring, and all hardware associated with providing power and communication between the local control cabinet and the sign.  It shall also include writing, providing, and installing all software and any needed hardware to ensure the VMS is fully compatible with and completely capable of being operated by the Contracting Agency's NG_TMS system. Toll signs maybe connected to the WSDOT NWG Traffic Management System for testing.

Power Supplies

The LED display matrix shall be powered by regulated switching DC power supplies that operate from 120 VAC input power and have an output of 24 volts DC or less.  Power supplies shall be wired in a redundant parallel configuration that uses multiple supplies per display.  The supplies shall have a “current sharing” capability, that allows them to provide equal amounts of current to their portion of the LED display.  Power supplies shall be rated such that if one supply fails, the remaining supplies will be able to operate their portion of the display under full load conditions (all pixels on at maximum drive current) while in an ambient temperature of +140° F.

Power supplies shall operate within a minimum input voltage range of +90 to +135 volts AC.   Power supply output at an ambient temperature of +140° F shall be no less than 65% of its room temperature (+70° F) output.  Power supply efficiency shall be a minimum of 74%.  Power supplies shall have a minimum power factor rating of 0.95.  Power supplies shall be short circuit protected.  Under short circuit conditions, the DC side of the power supply shall be powered down.  The power supplies shall reset automatically after 5 seconds of AC power off.  Power supplies shall be protected by a minimum overload allowance of 105%.  Inputs to power supplies shall be fused or circuit breaker protected.  A failed power supply shall not interfere with the other operating power supplies.

The VMS sign controller shall be capable of monitoring the operational status (“normal” or “failed”) of each individual power supply by reading a diagnostic signal located on the supply’s DC output.

A copy of the power supply manufacturer’s data sheet and its UL product card shall be provided with the VMS manufacturer’s submittal.

The VMS manufacturer’s submittal shall contain calculations demonstrating that the power supplies are rated for the criteria in this Special Provision.  These calculations shall account for power supply output de-rating at a temperature of +140° F.

Transient Current Protection

VMS and sign controller signal and power inputs shall be protected from electrical spikes and transients.

AC power for all equipment shall be protected at the load center inside the field cabinet.  A parallel-connection surge suppresser, rated for a minimum surge of 10 kJ, shall be connected to the load center in a manner that protects the load center and the equipment it feeds.

AC power for control equipment, such as the field controller and modem, shall be further protected by the use of a series-connected surge suppresser capable of passing 15 Amps of current.  This device shall be UL 1149 recognized.

EIA 232/485 communication ports in the sign controller shall be protected by avalanche diodes rated for 11.5 Volts at 10 Amps and 14 Volts at 70 Amps.  The diodes shall be and connected between each signal line and ground.

Digital input and output lines from the VMS to the control equipment shall be protected at the control equipment by optically isolated input and output modules, or optically-isolated solid state relays.  Inputs shall include, but shall not be limited to the VMS regulated power supply diagnostics and the AC power failure alarm.  Outputs shall include, but shall not be limited the cooling fan and defog/defrost fan control.

VMS Sign Controller

Each VMS shall include an associated sign controller, which shall be installed in the field cabinet as shown in the Plans. The sign controller hardware and software shall be manufactured by Daktronics and shall support all VMS communication, control, and diagnostic features as listed herein.

The following is a list of parts that shall be used for the variable  message signs controllers for this project, if the vendor has a newer product at the time of construction which supersedes these part numbers, the newer product shall be considered if it meets all the same standards:

1.	Vanguard VFC Controller

2.	Vanguard DDMS Controller

The VFC controller shall be able to control up to eight signs of the same size.

Memory

Sign controllers shall have both permanent and semi-permanent memory.  Permanent memory shall be EE-PROM integrated circuits and shall contain the executable sign controller software.  Semi-permanent memory shall be RAM integrated circuits with a battery backup that retains the data in memory for a minimum of one year following a power failure.  Semi-permanent memory shall contain the library of messages, the message display schedule and programmable operating parameters.  Each message shall have the capability to be defined and stored as a three-page message.

Power Interruptions

Contents of the sign controller’s memory shall be preserved by battery backup during AC power interruptions and the controller shall automatically resume operation once AC power is restored.  Upon recovering from a power interruption, the sign controller shall display the message identified by the Power Recovery Message parameter.  The sign controller shall report to the central computer that it has recovered from a power interruption.

Sign Controller Software

The sign controller shall cause the desired message to be displayed on the VMS.  The sign shall display alphanumeric character fonts.  The sign controller shall provide a default value for each NTCIP object supported.

Message Selection

The central computer or laptop computer shall cause the sign controller to implement a message selected from those stored in controller memory, or a new message entered via the communication port.

The sign controller shall incorporate CRC checks to verify MULTI strings. The sign shall not display a message unless the MessageActivationCode CRC matches the MessageCRC.

A message shall remain displayed on the sign until either a command to change the current message or a command to blank the display is received.  A command to display a message shall not succeed if the activation priority is less than the run time priority of the message currently displayed.

Data Transmission Requirements

Each sign controller shall contain two communication ports.  Each communication port shall be labeled (“Local” or “Central”) and shall be set to 9600 baud at the factory.  Each port shall operate independently at baud rates of 1200, 2400, 9600, and 19,200 bits per second.  The user shall select the baud rate for each port via a DIP switch.

Communication

The sign controller hardware and software shall communicate with the central computer in a polled multi-drop operation.  In the polled multi-drop operation, several sign controllers shall share the same communication channel, with each controller assigned a unique ID number.  Controller ID numbers shall conform to the NTCIP requirements for address numbers.  A sign controller shall only reply to messages labeled with its ID.   In polled multi-drop mode, sign controllers never initiate communication, but merely transmit their responses to messages from the central computer.

A laptop computer connected to the sign controller’s local communication port shall have the same control and diagnostic capabilities as the central computer.  However, local laptop control capability shall be limited to the VMS which is directly connected to that sign controller.

NTCIP Requirements

The sign controller software shall comply with the National Transportation Communications for ITS Protocol (NTCIP) documents and all related errata sheets published before July 1, 1999 and as referenced herein.

The sign controller software shall support the following standards:

1.	NTCIP 1101, Simple Transportation Management Framework (STMF), Conformance Level 1 (Simple Network Management Protocol (SNMP))

2.	NTCIP 2001, Class B Profile.  All serial ports on the device shall support communications according to these standards.

3.	NTCIP 2101, SP-PMPP/RS232 Point-to-Multi-Point Protocol (PMPP)

4.	NTCIP 2201, NTCIP TP-Null Transport Profile Null (TP-NULL)

The sign controller software shall implement all mandatory objects of all mandatory conformance groups as defined in NTCIP 1201, Global Object Definitions, and NTCIP 1203, Object Definitions for Dynamic Message Signs.  Software shall implement the following conformance groups:

NTCIP 1203, Object Definitions for DMS

1.	VMS Sign Configuration

2.	MULTI Configuration

3.	Default Message Control

4.	Pixel Service Control

5.	MULTI Error Control

6.	Sign Status

7.	Status Error

8.	Pixel Error Status

9.	Lamp Error Status

10.	Fan Error Status

11.	Power Status

12.	Temperature Status

The software shall implement the following optional objects:

NTCIP 1203, Object Definitions for DMS

1.	dmsMessageBeacon

2.	dmsMessagePixelService

3.	dmsCommunicationsLossMessage

4.	dmsPowerLossMessage

5.	dmsTimeCommLoss

6.	dmsMultiOtherErrorDescription

7.	dmsStatDoorOpen

8.	fanFailures

9.	fanTestActivation

10.	lineVolts

11.	tempMaxSignHousing

Objects required by these specifications shall support all values within its standardized range.  The standardized range is defined by a size, range, or enumerated listing indicated in the object’s SYNTAX field and/or through descriptive text in the object’s description field.  The following list indicates the modified object requirements for these objects.

| Object Name | Object ID | Minimum Requirements |
| --- | --- | --- |
| Number of Fonts | numFonts | 9 |
| Maximum Characters per Font | maxFontCharacters | 255 |
| Default Background Color | defaultBackgroundColor | 0 |
| Default Foreground Color | defaultForegroundColor | 9 |
| Default Justification Line | defaultJustificationLine | 2, 3, and 4 |
| Default Justification Page | defaultJustificationPage | 2, 3, and 4 |
| Number of Permanent Msgs. | DmsNumPermanentMsg. | 2 |
| Maximum No. Changeable Msg. | DmsMaxChangeableMsg. | 8 |
| Maximum Number Volatile Msg. * | dmsMaxVolatileMsg. | 8 |
| Control Mode | dmsControlMode | 2, 4, and 5 |

*	Changeable messages in excess of the minimum requirement are considered to meet the specification for an equivalent number of Volatile messages.

The first permanent message shall be used to blank the sign display.  The second permanent message shall be the diagnostic message.

Sign controller software shall implement the following tags (opening and closing where defined) of the Mark-Up Language for Transportation Information (MULTI) as defined in NTCIP 1203:

1.	Flash

2.	Font

3.	Justification Line

4.	Justification Page

5.	Moving Text

6.	New Line

7.	New Page

8.	Page Time

Documentation

Software shall be supplied with all documentation on 1.44Mb IBM-compatible diskette(s).  ASCII versions of the following Management Information Base (MIB) files in Abstract Syntax Notation 1 (ASN.1) format shall be provided on CD-ROM:

1.	The official MIB Module referenced by the device functionality.

2.	A manufacturer-specific version of the official MIB Module with the non-standardized range indicated in the SYNTAX field.  The filename shall match the official MIB Module, with the extension “spc”.

3.	A MIB Module of all manufacturer-specific objects supported by the device with accurate and meaningful DESCRIPTION fields and the supported ranges indicated in the SYNTAX field.

Control Software

This work shall consist of furnishing Variable Message Sign (VMS) control software.  The control software shall be a 32-bit or 64-bit application, designed to operate on Microsoft( Windows 7(or Server 2008( operating system.  The control software shall provide for command and control of the following functions:

VMS Control

Software shall retrieve, display, update and download/upload the following functional parameters to the local sign controller in response to user-initiated instructions.  The sign controller shall not perform pixel service tests when VMS are displaying messages.  Software shall perform the following operations in conjunction with its monitoring and logging functions:

Display a message

Blank the current message

Change message priority

Pixel service, lamp and fan tests

Set time and date in the sign controller

Retrieve sign controller ID, type, and manufacturer

Communications

Communications between the control software and sign controller shall be  NTCIP compliant, as indicated in the Special Provision for Variable Message Sign System.

The control software shall verify all communications for errors.  If a response from a sign controller contains a communication error, or if there is no response, the Control Software shall re-establish communications.

Data Collection

The control software shall retrieve errors detected, message number currently being displayed, and current message priority.  Using different commands, the software shall retrieve message MULTI strings, a map of defective pixels, the time and date, the event schedule, and configuration parameters.

Message Library

The control software shall store messages and transfer messages to a sign for storage and/or display.  When a user desires to send a message to a sign, the control software shall offer as choices only those messages compatible with the sign in question.  The control software shall allow message names of up to 25 characters in length.  If the selected name already exists, the software shall notify the user and give the option of replacing the existing message or selecting another name.

The control software shall display all character fonts supported by the Variable Message Sign System.  Messages shall be displayed on the computer monitor in exactly the same format (font, text centering and justification) as on the Variable Message Sign.

Software Duplication Rights

The Department shall have the right to duplicate the Variable Message Sign Control Software as needed for use in controlling signs under its jurisdiction.

Documentation

The Contractor shall furnish five (5) copies of the Control Software user manuals to the Engineer.  In addition, three (3) sets of the software, installation program, instructions and user manual shall be furnished on CD ROM or diskettes to the Engineer.

8-20.2.OPT8(B).ITS.DT1

(NWR ITS September 26, 2005)

Ground-mounted VMS Field Cabinet

The field cabinet shall contain the equipment shown in the Plans. The cabinet shall have the same external dimensions and appearance of Model 334 cabinets as specified in Chapter 12 of FHWA IP-78-16.  The cabinet shall contain the main power feed from the 120/240v transformer.

1.	Cabinets shall be fabricated of 0.125 inches sheet aluminum, 5052 alloy, with mill finish, in accordance with Section 9-29.13(7)D, Item number 1.  Painted or anodized aluminum is not allowed.

2.	Cabinet doors shall have a three-point latch and two-position stop assembly with spring-loaded construction core lock capable of accepting a Best Lock Company 6-pin CX series core.  The Contractor shall supply green construction cores with two master keys and one core removal key per lock.  The Contractor shall deliver the keys to the Engineer.

3.	The cabinet shall be equipped with an electric strip heater and a ventilation fan. The strip heater shall be rated at 100 watts and 120 VAC and be shielded in a manner that prevents damage to nearby electrical cables. The ventilation fan shall be mounted in the top of the cabinet, be equipped with a screened guard, and exhaust at least 10 CFM.

The fan and strip heater shall be controlled by a high-low adjustable thermostat, which can be set to ensure the cabinet interior temperature remains between 60(F and 120(F.

4.	Two shatterproof fluorescent interior cabinet lights with self-starting ballast shall be furnished, one fixture mounted on the rear rack near the top and the second mounted at the top of the front rack.  Door switches shall automatically turn on both lights when either door is opened.

5.	The cabinet shall be provided with two 15 amp, 120 VAC duplex receptacles.  One of the receptacles is for a laptop and/or tools and shall be GFCI-protected.  The second receptacle is for communications equipment and shall not be GFCI-protected.

6.	The cabinet shall be provided with three (3) circuit breakers. One circuit breaker shall be rated at least 20 amps and shall operate the heater, ventilation fan, receptacles, and lamps.  The second circuit breaker shall be two-pole and control the power to the VMS defog/defrost heater elements.  The third circuit breaker shall operate all other sign equipment.  The second and third circuit breakers shall be rated in accordance with the NEC.  Separate terminal strips shall be provided for each circuit breaker and an unfused terminal for the neutral side of the power supply line.

7.	The cabinet shall contain one VMS sign controller as specified under VMS Sign Controller.  The cabinet shall be provided with two serial communication ports.

One communication port shall be used to connect a laptop to the controller.  The interface shall be wired as a 9-pin, EIA-232 DCE port.  The port shall connect to a laptop computer using a straight-through 9-pin cable.  One cable shall be supplied for each VMS installed in this contract.

The second communication port is for remote control of the sign from the central computer.  The interface shall be wired as a 25-pin, EIA-232 DTE port.  This port connects to a communication interface (modem) specified elsewhere in this contract.  A cable shall be supplied to connect the VMS communication port to the modem port (the modem port may be a non-standard pin-out and require a custom-made cable).

A reset button shall be provided in the cabinet that, when pressed, resets the VMS controller and all other VMS electronics.

8.	A pullout shelf shall be provided in the cabinet to facilitate a laptop during local testing and control of the VMS.

9.	Noise and voltage spike protection shall be provided in the cabinet as stated in the Transient Current Protection section of the Contract Provisions.

10. The conductor within the cabinet and the sign shall meet the requirements of Section 9-29.24.  The conductors for communication shall be a minimum of 22 gauge.

8-20.2.OPT8(C).ITS.DT1

(NWR ITS September 26, 2005)

Control System

The VMS control system shall include all excavation, backfill, conduit, wiring, and all hardware associated with providing power and communication between the local control cabinet and the sign.  It shall also include writing, providing, and installing all software and any needed hardware to ensure the VMS is fully compatible with and completely capable of being operated by the Contracting Agency's existing Digital VAX computer system, while requiring no additional software or software modifications to be installed in the Contracting Agency's VAX.

Circuit Boards

The manufacturer’s submittal shall include a schematic diagram for each type of circuit board used in the sign display and control system.  Each circuit board used in the VMS display and control system shall conform to the following:

1.	The printed circuit board through-hole for each LED cathode lead shall be connected to a large copper trace pad having a minimum surface area of 0.04 square inch.  The trace pads shall dissipate heat from the LEDs and shall be present on both the front and rear sides of the LED pixel board.

2.	All exposed metal (except connectors) shall be protected from water and humidity exposure by a thorough application of acrylic conformal coating.  Bench level repairs to individual devices, including discrete LED replacement and conformal coating repairs, shall be possible.

3.	Printed circuit laminate shall be FR-4 fiberglass, having a minimum thickness of 1/16 inch.  The circuit board traces shall be copper.  Through-holes shall also be plated with copper.

4.	All cables attaching to circuit boards shall be held in place by locking latch connectors that firmly hold the cables in place.

Display LEDs

LEDs used in the VMS display shall be from one LED manufacturer and of one part number.  LEDs shall conform to the following minimum requirements:

1.	LEDs shall be un-tinted, non-diffused, high-output, solid state lamps utilizing Indium Gallium Aluminum Phosphide (InGaAlP) technology.  The LED manufacturer shall be Toshiba or Hewlett-Packard.

2.	The discrete LEDs size shall be T 1-3/4.  LED package style shall be the through-hole flush-mount type, and all LEDs shall be soldered with the base of their lens mounted within 0.010 inches of the printed circuit board.

3.	LEDs shall emit amber light, having a peak wavelength of 590 ( 5 nanometers.  The half-life rating shall be 100,000 hours. Rated brightness per LED shall be a minimum of three (3) candelas.

4.	LEDs shall be pre-sorted by the LED manufacturer for luminous intensity and color.  LEDs used shall be obtained from a one-bin luminous intensity sort.  A bin is defined such that when all LEDs from a given bin are driven with an identical forward current, the dimmest LED shall emit no less than half the luminous intensity of the brightest LED in the bin.

5.	Operating temperature range shall be -22 to +185° F, and storage temperature range shall be -40 to +248° F.

6.	Minimum half-power viewing angle shall be 15°.  Half-power viewing angle is defined such that, at a given distance from the LED, luminous intensity measured at any point at an angle of 7.5° from the LEDs center axis shall be no less than half the luminous intensity measured directly on the LEDs center axis.

7.	The discrete LED manufacturer’s data sheet showing compliance with this Special Provision, and 10 samples, shall be provided with the VMS manufacturer’s submittal.

LED Modules

The VMS shall be constructed with multiple display circuit boards, each of which contains no less than five (5), but no more than forty-five (45) pixels.  Each pixel, which is defined as the smallest programmable portion of a display matrix, shall consist of a cluster of closely spaced discrete LEDs (strings of LEDs) and shall conform to the following requirements:

1.	The distance from the center of one pixel to the center of all adjacent pixels, both horizontally and vertically, shall be 66.0 millimeters.

2.	Each LED string shall be in series with its own current limiting resistor.  Current limiting resistors shall be rated to limit LED string forward current to 30 milliamperes whenever a forward voltage is applied.

3.	Each pixel shall contain a minimum two (2) string of LEDs.  Each LED string shall contain a minimum six (6) LEDs.

4.	The failure of an LED string shall not cause a change in the forward current of any other LED string, nor shall it cause the failure of any other LED string.  Similarly, the failure of any LED pixel shall not cause the failure of any other pixel in the VMS.

5.	Each LED pixel shall emit a minimum luminous intensity of 40 candelas when driven with a forward current of 20 milliamperes DC per LED string.  An independent laboratory that utilizes equipment and procedures traceable to N.I.S.T. standards shall certify LED pixel intensity.  The independent laboratory’s certification report shall be provided with the VMS manufacturer’s submittal.  This report shall contain the laboratory name, address, and contact information.  The report shall also contain a description of the test procedure and test equipment used, test personnel name(s), pixel intensity test results, date(s) the VMS manufacturer’s LED pixel samples were tested, and the VMS manufacturer’s name.

6.	Discrete LEDs shall be mounted perpendicular to their PC boards.  Any variations in discrete LED color and intensity shall be thoroughly dispersed throughout the entire display, thereby creating a uniform visual appearance of both color and intensity.

7.	The sign controller shall be able to measure the forward current of each LED pixel and determine if the pixel is operating normally.  This information shall be stored in a read-only NTCIP object.

LED Output Control

The LEDs shall be driven using Pulse Width Modulation (PWM) of a nominal 30 milliampere forward current, where pulse width is used to achieve the programmed LED intensity level for a given ambient lighting condition.

The current pulse shall be modulated from a 10-millisecond period, and pulse amplitude shall not be allowed to exceed 30 milliamperes per LED string.  An illustration of the PWM drive current waveforms, which are used to achieve minimum and maximum LED intensity, shall also be provided with the VMS manufacturer’s submittal.

LED Intensity Control System

The VMS shall be equipped with an LED intensity control system.  The control shall support both manual and automatic control.  LED intensity control shall consist of three (3) photo-sensors and associated circuitry.  VMS controller analysis of these ambient light measurements shall automatically determine which of sixteen pre-programmed LED intensity levels will provide the best VMS legibility for the given ambient light condition. The LED intensity control system shall not cause flickering of the LED display.

The LED intensity control system shall conform to the following minimum requirements:

1.	The VMS controller shall contain a read-write NTCIP object that adjusts the maximum usable intensity threshold, the Maximum Pulse Width Modulation (MPWM).  This number is a percentage of the absolute maximum possible intensity.  At the time of VMS delivery, MPWM shall be set to 67%.  The LED intensity control system shall be designed such that a MPWM value of 100% delivers a time-average current of 30 milliamperes, and the MPWM value of 67% delivers a time-average current of 20 milliamperes.

2.	Automatic intensity control shall select one of sixteen LED intensity levels based on the sensed ambient light.  The threshold points for each intensity levels shall be user programmable.  LED intensity levels shall be available in 1% increments and in a range of 1% to 100% of maximum display intensity.

LED Display Driver Circuit Boards

The VMS shall contain 9x5 LED display modules, which are constructed as follows:

1.	LED pixel circuit boards shall be mounted to the back of an aluminum panel to form a 9 pixel high by 5 pixel wide LED display module.  The pixel board(s) shall be mounted to the aluminum panel with durable, non-corrosive fasteners, and their removal from the panel shall not require use of tools.

2.	One electronic driver circuit board shall be provided for each 9 high by 5 wide (9x5) LED pixel module and shall individually control all 45 pixels on that module.

3.	Failure of a 9x5 driver board shall not cause the failure of any other 9x5 LED display module.

4.	The LED display shall have a minimum refresh rate of 100 frames per second.  The VMS manufacturer’s submittal shall provide calculations that prove that the display conforms to this requirement.

5.	The aluminum module panel shall have a minimum thickness of 1.5 millimeters, and it shall contain a circular opening for each LED pixel.  The openings shall be sized so they do not block any portion of the 15° LED viewing cone.

6.	The front side of the aluminum module panel, which faces the viewing motorists, shall be primed and coated with flat black paint.

7.	Display modules and all of their components shall be easily replaceable from inside the VMS housing.  Display modules shall mount securely to a support frame located inside the sign housing using durable, non-corrosive hardware.  Module removal and replacement shall be accomplished with the use of simple hand tools or no tools.

8.	All display module electrical connections shall be the quick-disconnect locking connector type.  Removal of a 9x5 display module from the VMS, or a pixel board or driver board from its display module, shall not require a soldering operation.

Power Supplies

The LED display matrix shall be powered by regulated switching DC power supplies that operate from 120 VAC input power and have an output of 24 volts DC or less.  Power supplies shall be wired in a redundant parallel configuration that uses multiple supplies per display.  The supplies shall have a “current sharing” capability, that allows them to provide equal amounts of current to their portion of the LED display.  Power supplies shall be rated such that if one supply fails, the remaining supplies will be able to operate their portion of the display under full load conditions (all pixels on at maximum drive current) while in an ambient temperature of +140° F.

Power supplies shall operate within a minimum input voltage range of +90 to +135 volts AC.   Power supply output at an ambient temperature of +140° F shall be no less than 65% of its room temperature (+70° F) output.  Power supply efficiency shall be a minimum of 74%.  Power supplies shall have a minimum power factor rating of 0.95.  Power supplies shall be short circuit protected.  Under short circuit conditions, the DC side of the power supply shall be powered down.  The power supplies shall reset automatically after 5 seconds of AC power off.  Power supplies shall be protected by a minimum overload allowance of 105%.  Inputs to power supplies shall be fused or circuit breaker protected.  A failed power supply shall not interfere with the other operating power supplies.

The VMS sign controller shall be capable of monitoring the operational status (“normal” or “failed”) of each individual power supply by reading a diagnostic signal located on the supply’s DC output.

A copy of the power supply manufacturer’s data sheet and its UL product card shall be provided with the VMS manufacturer’s submittal.

The VMS manufacturer’s submittal shall contain calculations demonstrating that the power supplies are rated for the criteria in this Special Provision.  These calculations shall account for power supply output de-rating at a temperature of +140° F.

Transient Current Protection

VMS and sign controller signal and power inputs shall be protected from electrical spikes and transients.

AC power for all equipment shall be protected at the load center inside the field cabinet.  A parallel-connection surge suppresser, rated for a minimum surge of 10 kJ, shall be connected to the load center in a manner that protects the load center and the equipment it feeds.

AC power for control equipment, such as the field controller and modem, shall be further protected by the use of a series-connected surge suppresser capable of passing 15 Amps of current.  This device shall be UL 1149 recognized.

EIA 232/485 communication ports in the sign controller shall be protected by avalanche diodes rated for 11.5 Volts at 10 Amps and 14 Volts at 70 Amps.  The diodes shall be and connected between each signal line and ground.

Digital input and output lines from the VMS to the control equipment shall be protected at the control equipment by optically isolated input and output modules, or optically-isolated solid state relays.  Inputs shall include, but shall not be limited to the VMS regulated power supply diagnostics and the AC power failure alarm.  Outputs shall include, but shall not be limited the cooling fan and defog/defrost fan control.

VMS Sign Controller

Each VMS shall include an associated sign controller, which shall be installed in the field cabinet. The sign controller hardware and software shall support all VMS communication, control, and diagnostic features as listed herein.

Memory

Sign controllers shall have both permanent and semi-permanent memory.  Permanent memory shall be EE-PROM integrated circuits and shall contain the executable sign controller software.  Semi-permanent memory shall be RAM integrated circuits with a battery backup that retains the data in memory for a minimum of one year following a power failure.  Semi-permanent memory shall contain the library of messages, the message display schedule and programmable operating parameters.  Each message shall have the capability to be defined and stored as a three-page message.

Power Interruptions

Contents of the sign controller’s memory shall be preserved by battery backup during AC power interruptions and the controller shall automatically resume operation once AC power is restored.  Upon recovering from a power interruption, the sign controller shall display the message identified by the Power Recovery Message parameter.  The sign controller shall report to the central computer that it has recovered from a power interruption.

8-20.2.OPT12.ITS.docx

Active Traffic Management System

(******)

All new LCS, SDMS, and VMS sign display and control cabinet to be installed in the project as identified on the Plan shall comply with all material requirements in subsection Variable Message Sign special provision.

8-20.2.OPT13.ITS.DT1

Highway Advisory Radio (HAR) System

8-20.2.OPT13(A).ITS.DT1

(NWR ITS October 16, 2006)

Highway Advisory Radio Transmitter (HART)

Each HART shall be a Black Max HAR AM Broadcast System, manufactured by Highway Information Systems, Inc.  The HAR system shall include the following components:

1.	Equipment Model Numbers:

Electronics Rack	RCK0001

AM Transmitter Module	DRTXM3

Digital Recorder Module	DR1500AM

Digital Communications Controller Module	DCC-1

Power Supply Module	DRPSM1

Antenna	ANT1000

Ground Plane	GND0001

2. 	Manufacturer Information:

Highway Information Systems, Inc.

4021 Stirrup Creek Dr

Suite 100

Durham, NC  27703

Telephone: 1-800-849-4447

www.highwayinfo.com

3.  	Equipment Descriptions:

Amplitude Modulated (AM) Transmitter Module

The amplitude modulated transmitter module shall be of a FCC-accepted type and operate on a frequency of *** $$1$$ ***.  The transmitter module shall be installed in a RCK0001 equipment rack.

Digital Recorder Module

The digital recorder module records and plays back human voice messages by the use of a solid-state memory.  The module shall be installed in a RCK0001 equipment rack.

Digital Communications Controller Module

The digital communications controller module allows the user to control the HART using touch-tone telephone, various serial interfaces, and ethernet.  The module shall be installed in a RCK0001 equipment rack.

Antenna

The antenna system shall match the transmitter frequency.  The antenna shall be such that it can be tuned to resonance at mounting heights between 25 and 30 feet above the ground.  The antenna shall be rugged and able to withstand winds of up to 80 mph without ice buildup, and 50 mph with 1/2-inch of ice buildup.

The antenna shall be mounted on a wood pole as shown in the Plans with appropriate hardware.

The antenna system shall include the installation of a groundplane consistent with the manufacturer’s recommendation.  This ground plane shall be either the Triad Ground System (consisting of 6, 10 foot long perforated copper ground pipes buried 20 feet deep) or the Radial Ground System (consisting of 20 – 120 foot long 8 AWG copper radials buried 1 foot deep).

HART Cabinet

The HART Cabinet shall be a Model 334 Controller Cabinet meeting the requirements of the subsection Fiber Optic Terminal Cabinets of these specifications.

Communication Connection

Where twisted-pair cable is installed in the HART cabinet, the following shall be provided:

1.	Type R66B, six-pair, six-position, quick-connect terminal block.  Each block shall contain 12 rows with six clips each.

Type RJ11 jack.

Where fiber optic cable is installed in the HART cabinet, the following shall be provided:

1.	Fiber Optic Ethernet switch (as identified in the Plans and specified in Voice, Video and Data Distribution and Transmission Systems)

2.	Fiber Optic Distribution Panel (as identified in the Plans and specified in Fiber Optic Distribution Panels)

8-20.2.OPT13(B).ITS.DT1

(NWR ITS February 23, 2009)

Flashing Beacons

Two 8-inch amber beacons with round visors shall be provided with each sign assembly.  The signal display shall meet the requirements of Section 9-29.16.  The flashing beacon control shall meet the requirements of Section 9-29.15.  The beacons shall flash alternately. The flashing control shall be designed to be accessible from inside the cabinet.

Sign Lighting Luminaires

The sign lighting luminaires shall consist of standard sign lights in accordance with Standard Plan G-9 except for the shoulder mount sign, where the sign light shall be mounted on top.  The Contractor shall include a top mount kit for the sign light for this location.

Model 334 Cabinet

Controller cabinet furnished shall meet the requirements specified in Chapter 6 of the Caltrans Traffic Signal Control Equipment Specifications (TSCES), January 1989, as currently amended except as modified by the following:

Cabinet Construction

1.	Cabinets shall be fabricated of 0.125-inch sheet aluminum, 5052 alloy, with mill finish, in accordance with Section 9-29.13(7)D, Item number 1.  Painted or anodized aluminum is not allowed.

2.	A spring loaded construction core lock capable of accepting a Best 6-pin core shall be installed on all doors accessing WSDOT equipment. A 6-pin green construction core shall be installed in each core lock. Upon contract completion, two master keys for each cabinet shall be delivered to the Engineer.

Cabinet Ventilation and Heating

1.	A 12 inch wide x 16 inch high x 1 inch thick disposable paper filter element shall be provided in lieu of a metal filter.

2.	The cabinet shall be equipped with an electric strip heater with a rating of 100 watts and 120 VAC, and a ventilation fan meeting the requirements specified in Chapter 6 of Caltrans TSCES, 1989.  The strip heater shall be shielded in a manner that prevents damage to nearby electrical cables.

3.	The fan and strip heater shall be controlled by a high-low adjustable thermostat that can be set to ensure the cabinet interior temperature remains between 60(F and 125(F

Cabinet Accessories

The Contractor shall provide all cabinet accessories, including:

1.	Two shatterproof fluorescent interior cabinet lights with self-starting ballast shall be furnished, one fixture mounted on the rear rack near the top and the second mounted at the top of the front rack.  Door switches shall automatically turn on both lights when either door is opened.

2.	One controller unit shelf, which attaches to the front rails of the EIA rack, shall be provided in lieu of the two controller unit support angles.  The shelf shall be fabricated from aluminum and shall be installed such that it does not interfere with access to any terminal block.  The shelf shall contain a roll-out flip-top drawer for storage of wiring diagrams and manuals.

3.	Each Model 334 cabinet shall be equipped with a fully operable Type 170E controller equipped as specified in these Special Provisions.

4.	A transient voltage protection device shall be provided, which plugs into the controller unit receptacle and in turn accepts the controller plug and meets the electrical requirements of Section 9-29.13(7)B(3)e.

5.	The cabinet shall be equipped with a power distribution panel mounted in a standard EIA 19-inch (ANSI/EIA RS-310-C) rack utilizing no more than five rack-mounting spaces (8.75 inches).  The following devices shall be provided with the power distribution panel:

a.	Duplex 120 VAC power receptacle.

b.	Main circuit breaker, 120 VAC, 20 amp.

c.	Four load circuit breakers, 120 VAC, 15 amp.

d.	Neutral bus

e.	Ground Bus

f.	Surge suppresser and filter unit 120 VAC, 50 amp.

The ground bus, neutral bus, and surge suppresser and filter unit shall be mounted on the right rear cabinet panel.  All other power distribution panel components shall be mounted in or on the panel such that they are readily accessible, provide dead front safety, and all hazardous voltage points are covered to prevent inadvertent contact.

6.	Each Cabinet shall be furnished with a mounting panel.  The mounting panel shall be fabricated from aluminum and shall be 19 inches wide by 10.5 inches tall.

7.	The mounting panel shall be equipped with one HAR sign control switch with labels and functions as follows:

AUTOMATIC

Flashing Beacons shall energize upon ground true call from controller.

SIGN OFF

Flashing Beacons shall de-energize.

SIGN ON

Flashing Beacons shall energize.

8.	The sign relay shall be plugged into a socket installed on the rear of the mounting panel.  The relay shall be wired as shown in the Plans.  The relay coil shall draw (or sink) less than 50 milliamperes from the 170E controller and have a DPDT contact rating not less than 10 amperes.  A 1N4004 diode shall be placed across the relay coil to suppress voltage spikes.

9.	The Contractor shall install the C1 connector according to the pin assignments shown in the Plans.

10.	One reproducible drafting film and two non-fading copies of the cabinet wiring diagram shall be furnished with each cabinet.

11.	Each HAR sign cabinet shall be supplied with one Model 204 sign flasher unit mounted on the right rear side panel.

12.	The Contractor shall provide and install a rack-mounted fiber optic distribution panel as identified in the Plans.

13.	The Contractor shall provide and install a communication device as shown in the Plans and as specified in these Special Provisions.  The Contractor shall also provide and install the cable between the communication device and the C-2 plug of the model 170E controller.

Cabinet Wiring

1.	Cabinet wiring shall conform to the details and diagrams in the Plans.  The Contractor shall trim wiring to eliminate all slack and lace or bind together with nylon wraps or equal.  All terminals shall be labeled.  The cabinet shall be wired completely so that the only requirement to make a field location completely operational is to connect field, power and ground wires to appropriate terminals.

2.	Terminal block TB1 shall be installed in the cabinet.

Terminals for field wiring shall be labeled, numbered and connected in accordance with the following:

Terminal	Terminal and	Connection

Block Pos	Wire Numbers	Identification

TBS	501-502	AC Power, Neutral

TB1-1	644	Flasher Output NC

TB1-2	645	Flasher Output NO

TB1-3		Future Neutral

Model 170E Controller

Each HAR sign controller unit furnished shall meet the requirements specified in Chapter 2 of the Caltrans Transportation Electrical Equipment Specification (TEES), August 2002, as currently amended and modified as follows:

1.	The 170E CPU module shall operate a 68HC11F1 MPU at a crystal frequency of 8MHz.  The MPU shall be socket mounted in a PLCC socket.

2.	The EPROM shall be resident on the CPU module.  The EPROM socket shall be a 32-pin lever-controlled ZIF device.  The EPROM shall be either a 32K x 8 or a 128K x 8 device.  The device size shall be jumper selectable.

3.	Feature and Location switches shall be provided on the front portion of the CPU module.  Each switch shall be an 8-position front-reading dip switch.  The switches shall be addressed as follows:

Location Switch at 7000 (Port A)

Feature Switch at 700A (Port E)

4.	There shall be one LED indicator located on the front of the CPU module.  This LED shall be connected to bit 3 of Port G.

5.	The 170E controller shall have a minimum of 28 kB of battery backed static RAM on the CPU module.  RAM shall be continuous from location 0000 to 6FFF.

6.	Four Asynchronous Communication Interface Adapters (ACIAs) shall be provided on the same board as the CPU.  The ACIAs shall be 6850 ICs operating at a crystal frequency of 6.144MHz.  Each ACIA shall have 5 programmable jumpers to select 5 communication baud rates (1200, 2400, 4800, 9600, 19200) for a total of 20 jumpers.  All ACIAs shall be active.  An IRQ status register shall be provided at 75FF.

7.	The Model 412C PROM module shall not be provided.  A blank panel shall cover the PROM slot.

8.	Two blank 27256 EPROM chips shall be provided with the CPU module.

8-20.2.OPT13(B)3.ITS.DT1

(NWR ITS February 23, 2009)

10.	Each 170E controller shall include an unmanaged ethernet switch and a cabinet device server.

8-20.2.OPT14.ITS.DT1

Communication Conduit System

8-20.2(9-29.1).DT1

Conduit, Innerduct, and Outerduct

8-20.2(9-29.1).INST1.ESP.DT1

Section 9-29.1 is supplemented with the following:

8-20.2(9-29.1).OPT1.ESP.DT1

(NWR May 5, 2014)

Conduit Sealing

Cabinet conduit sealing shall be one of the following:

1.	Duo-fill 400 – self expanding waterproof foam

2.	Jackmoon – Triplex Duct Plugs

3.	O-Z Gedney – Conduit Sealing Bushings

Mechanical plugs shall be installed per manufacturer’s recommendations.

8-20.2(9-29.1(2)).DT1

Rigid Metal Conduit Fittings and Appurtenances

8-20.2(9-29.1(2)).INST1.ESP.DT1

Section 9-29.1(2) is supplemented with the following:

8-20.2(9-29.1(2)).OPT1.ESP.DT1

(August 10, 2009)

Conduit Coatings

Electroplated couplings are not allowed.

8-20.2(9-29.1(2)).OPT2.ESP.DT1

(NWR March 4, 2009)

Surface Mounting Conduit Attachment Components

Channel supports and all fastening hardware components shall be Type 304 stainless steel.  Conduit clamps shall be one piece, two bolt units with lock washers.

8-20.2.OPT14(D).ITS.DT1

(NWR ITS March 22, 2004)

Cable Vaults and Pull Boxes

Cable vaults and pull boxes shall meet AASHTO M-199, H-20 or H-35 loading requirements.  Cable vaults and pull boxes installed in paved shoulders or lanes that will be subjected to vehicular traffic during any phase of this contract or as specified in the Plans shall meet H-35 loading requirements.  Cable vaults and pull boxes shall be fabricated in accordance with ASTM C857-83 and C858-83.  All cable vaults and pull boxes shall include the following provisions:

1.	A sump 6 inches in diameter by 2 inches in depth with a 1-inch diameter drain hole in the center of the sump.

2.	Cable pulling irons positioned to afford bi-directional cable installation through the cable vault or pull box.

3.	Factory installed knock-outs for conduit entry.

4.	All cable racking hardware shall be stainless steel.

5.	Cable vaults meeting H-20 requirements shall have a hinged and spring-assisted double steel plate cover.  Cable vaults and pull boxes meeting H-35 requirements shall have round cast iron lids.  Pull boxes meeting H-20 requirements shall have a hinged, single plate cover.  All cable vault and pull box covers shall be marked with ITS legend according to Standard Plan J-11a.

Above ground pull boxes shall be a minimum 16 inches wide, 16 inches high and 8 inches deep, unless otherwise specified in the Plans.  Above-ground boxes shall be fabricated in accordance with NEMA 4X designation for stainless steel enclosures.  Pull boxes shall be equipped with a removable front panel for access to all conduits.  The front panel shall be hinged and the entire pull box shall be fabricated from stainless steel.

8-20.2.OPT18.ITS.DT1

Communication Cables And Interfaces

8-20.2.OPT18(A).ITS.DT1

(NWR ITS October 16, 2006)

Fiber Optic Distribution Panels

The fiber optic distribution panel shall be rated by the manufacturer as a fiber optic distribution panel. The distribution panel shall be designed to hold, at a minimum, the specified number of interconnection sleeves and splice trays. The splice trays and the fiber optic interconnection sleeves shall be fully enclosed on all sides by the distribution panel when the distribution panel is closed.

Each distribution panel shall be fully populated with interconnection sleeves.  Interconnection sleeves shall contain zirconium (ceramic) linings (phosphorus bronze is not allowed).  All unutilized interconnection sleeves shall have protective dust covers installed.

The distribution panels shall be EIA 19-inch (ANSI/EIA RS-310-C) rack-mountable, unless otherwise noted.

Mounting plates for interconnection sleeves shall be constructed of metal.  Adequate spacing shall be provided around each interconnection sleeve.  Where interconnection sleeves are arranged in a vertical line, the minimum horizontal center-to-center spacing shall be 1.25 inches (31mm), and the minimum vertical center-to-center spacing shall be 0.625 inches (16mm).  Where interconnection sleeves are arranged in a staggered layout, the minimum center-to-center radial distance between sleeves shall be 0.875 inches (22mm).

A wiring diagram shall be supplied with each distribution panel. The wiring diagram shall identify each fiber terminated in the distribution panel using the fiber optic cable labeling method as specified later in these provisions. The wiring diagram shall be placed in a plastic sheet protector next to the distribution panel.

8-20.2.OPT18(D).ITS.DT1

(NWR ITS October 16, 2006)

Cabinet Fiber Optic Distribution Panel

The fiber optic distribution panel shall be designed to hold a minimum of 36 FC fiber optic interconnection sleeves and splice trays with 48-splice capacity.  The distribution panel shall allow for full access to the splice trays and both sides of the fiber optic interconnection sleeves from the front of the distribution panel.  The distribution panel shall not exceed 3 RMU (5.25 inches) in height.

8-20.2.OPT18(F).ITS.docx

(******)

Preterminated Patch Panel

A wiring diagram shall be supplied with each patch panel.  The wiring diagram shall identify each fiber terminated in the distribution panel using the fiber optic cable labeling method as specified later in these provisions.  The wiring diagram shall be placed in a plastic sheet protector next to the distribution panel.

The Contractor shall provide, install and connect preterminated patch panels as shown in the Plans.  The panels shall be manufactured by Wesco/CSC – Communications Supply Corp.  Outside plant cable meeting ITU G652.D and G694.2 shall be utilized for the stubs on all preterminated patch panels and the Contractor shall confirm with the manufacturer that the length of each stub is sufficient for the needs at each location.  All openings in the patch panels shall be plugged by the manufacturer.  Connections shall be LC\UPC type and shall be terminated by the manufacturer.

1.	Equipment Model Numbers (for use in cabinets):

| Description | Part Numbers (Both parts are required) |
| --- | --- |
| 12-Port Preterminated Patch Panel | ADC12CLCXXXMCD00, and FL2-ACC0071 |
| 24-Port Preterminated Patch Panel | ADC24CLCXXXMCD00, and FL2-ACC0072 |
| 48-Port Preterminated Patch Panel | ADC48CLCXXMCD00, and FL2-ACC0072 |
| 72-Port Preterminated Patch Panel | ADC72CLCXXXMCC00, and FL2-ACC0073 |
| 96-Port Preterminated Patch Panel | ADC96CLCXXXMCC00, and FL2-ACC0074 |

Equipment Model Numbers (For concrete or underground Hubs):

| Description | Part Numbers (Both parts are required) |
| --- | --- |
| 48-Port Preterminated Patch Panel | ADC48CLCXXXDU00, and FL2-ACC0072 |
| 72-Port Preterminated Patch Panel | ADC72CLCXXXMDU00, and FL2-ACC0073 |
| 96-Port Preterminated Patch Panel | ADC96CLCXXXMDU00, and FL2-ACC0074 |

Note:	The stub length for each panel (XXX in the part number, in meters) shall be determined by the Contractor for each location and shall include 50 feet of slack in the cable vault.

2.	Manufacturer Information:

Wesco/CSC – Communications Supply Corp.

951 Monster Road

Renton, WA 98057

Tel: (425) 203 – 7881

Fax: (425) 793 - 5448

8-20.2.OPT18(G).ITS.DT1

(NWR ITS August 12, 2013)

Fiber Optic Connector

Unless otherwise noted in the Plans, all fiber optic connectors used on this project shall meet the following:

All shall be LC/UPC (55dB) in accordance with Telcordia 6R-326

All shall be factory-connectorized

8-20.2.OPT18(H).ITS.DT1

(NWR ITS February 11, 2002)

Fiber Optic Cable Lubricant

Fiber optic cable lubricant shall be as follows:

Compatible with the cable jacket

Non-combustible

Water-based leaving little or no residue

8-20.2.OPT18(I).ITS.docx

(******)

Fiber Optic Splice Closure

All fiber optic splice closures shall be re-enterable and reusable and be designed for use on fiber optic cables in an underground, submerged environment. Splice closures shall meet the following requirements:

- Rated for 1310 and 1550 nanometer wavelengths.

- Contain a valve to allow pressurization of the housing.

Fiber optic splice closures installed in a pull box shall meet the above requirements, be a maximum of 18 inches in length, and have all cables enter the same end of the closure.

8-20.2.OPT18(L).ITS.DT1

(NWR ITS October 16, 2006)

Fiber Optic Terminal Cabinets

Fiber optic terminal cabinets furnished for this contract shall be pad mounted and have the same external physical dimensions and appearance as Model 334 cabinets. Fiber optic terminal cabinets shall be fabricated in accordance with Section 9-29.25 except:

1.	Cabinets shall be fabricated of 0.125” sheet aluminum, 5052 alloy, with mill finish, in accordance with Section 9-29.13(7)D, Item number 1.  Painted or anodized aluminum is not allowed.

2.	Cabinet doors shall have a three-point latch and two-position stop assembly with spring loaded construction core lock capable of accepting a Best Lock Company 6-pin CX series core. The Contractor shall supply green construction cores. Upon substantial completion, the Contractor shall deliver two master keys and one core removal key to the Engineer.

3.	The cabinet shall be equipped with an electric strip heater with a rating of 100 watts and 120 VAC and a ventilation fan meeting the requirements specified in Chapter 12 of FHWA IP-78-16.

The fan and strip heater shall be controlled by a high-low adjustable thermostat that can be set to ensure the cabinet interior temperature remains between 60°F and 125°F.  The heater strip shall be shielded.

4.	Two shatterproof fluorescent interior cabinet lights with self-starting ballast shall be furnished, one fixture mounted on the rear rack near the top and the second mounted at the top of the front rack. Door switches shall automatically turn on both lights when either door is opened.

5.	The cabinet shall be equipped with a power distribution panel mounted on a standard EIA 19-inch (ANSI/EIA RS-310-C) rack utilizing no more than five RMU (8.75 inches).  The following devices shall be provided with the power distribution panel:

a.	Duplex 120 VAC power receptacle.

b.	Main circuit breaker, 120 VAC, 50 amp.

c.	Four load circuit breakers, 120 VAC, 15 amp.

d.	Neutral bus.

f.	Ground bus.

g.	Surge suppresser and filter unit, 120 VAC, 50 amp.

Power distribution panel components shall be mounted in or on the panel such that they are readily accessible, provide dead front safety, and all hazardous voltage points are covered to prevent inadvertent contact.

6.	One controller unit shelf, which attaches to the front of rails of the EIA rack, shall be provided. The shelf shall be fabricated from aluminum and shall contain a roll-out flip-top drawer for storage of wiring diagrams and manuals.

7.	The Contractor shall provide and install a rack-mounted, preterminated, fiber optic patch panel as identified in the Plans.

8-20.2.OPT19.ITS.DT1

Video, Voice, & Data Distribution And Transmission Systems

8-20.2.OPT19(A).ITS.DT1

(NWR ITS February 11, 2002)

If any equipment specified in this section has been superseded by a newer product that is interchangeable, the newer product shall be supplied.  If the product is no longer available and has no replacement, the Contractor shall propose a different product meeting the same performance and material specifications as the discontinued one.

8-20.2.OPT19(B).ITS.DT1

(NWR ITS October 16, 2006)

Video, Voice, & Data Distribution And Transmission System Cabling

The Contractor shall provide and install all required equipment interconnection cabling to include T1 cables, data cables, RG-59/U video coaxial cables, power cables, ancillary cables, and connectors as recommended by the equipment vendor at the cabinet locations and at the TMC. Conductors shall be of all copper construction.

The Contractor shall provide and install fiber optic patch cords between the fiber optic distribution panels and the equipment specified herein where singlemode fiber optic cable is utilized as the transmission medium.

8-20.2.OPT19(C).ITS.DT1

(NWR ITS February 23, 2009)

Video, Voice & Data Distribution Equipment

Video, voice, and data distribution equipment shall be manufactured by Optelecom, Inc.

1.	Equipment Model Numbers:

Digital Video Transmitter (stand-alone)	9225DT/SM-FC

Digital Video Receiver	9221DR/SM-FC

Drop/Insert Data Modem	9522A-LD-FC

Network Interface Card	9942A

Network Interface Software	9900-NMS

Hub Chassis	9002

Cabinet Chassis	9003-2

Power Supply (for Hub Chassis)	9030B

AC/DC Adapter (for Cabinet Chassis)	9010PS

AC/DC Adapter (for 9225DT)	9014PS

2.	Manufacturer Information:

Optelecom Inc.

12920 Cloverleaf Center Dr.

Germantown, MD  20874

Telephone:  (301) 444-2200

8-20.2.OPT19(F).ITS.docx

(******)

# Ethernet Communication Equipment

Ethernet communication equipment shall be manufactured by RuggedCom, Inc. and installed in each cabinet and Communication Hub as shown in the Plans. Equipment shall be conformal coated and include a power cord.

# 1.	Equipment Model Numbers

8-port Ethernet Switch			RS900-HI-D-L2-L2-00

9-port Ethernet Switch			RS900-HI-D-L2-L2-L2

10-port Gigabit Ethernet Switch		RS900G-HI-D-2LC25

19-port Gigabit Ethernet Switch               	RSG2100-F-RM-HIP-HIP-							TX01-TX01-TX01-TX01- 							CG01-TX01-FX06-C01

Ethernet Switch with Device Server	RS910-HI-D-S1-FX06-TX

Cabinet Device Server			RMC30-HI

Conformal Coating			82-01-0002

Power Cord				43-10-0008

# 2.	Manufacturer

RuggedCom, Inc.

30 Whitmore Rd

Woodbridge, Ontario, Canada L4L 7Z4

Tel: (905) 856-5288  Fax: (905) 856-1995

Toll Free: (888) 264-0006

www.ruggedcom.com

8-20.2.OPT19(H).ITS.DT1

(NWR ITS April 10, 2006)

MPEG4 Encoder/Decoder

The MPEG4 Encoder/Decoder shall be manufactured by Radiant Communications Corporation. The Contractor shall provide and install MPEG4 Encoder units in the camera cabinet as shown in the Plans and MPEG Decoder units in the Dayton Avenue Traffic Systems Management Center (TSMC).

1.	Equipment Model Numbers:

Encoder:  V3510-T-1U

Decoder:  V3520-R-1U

2.	Manufacturer Information:

Radiant Communication Corporation

5001 Hadley Road

South Plainfield, NY  07080

Tel: (908) 757-7444	Fax: (908) 757-8666

Toll Free: (800) 969-3427

www.rccfiber.com

8-20.2.OPT19(I).ITS.DT1

(NWR ITS October 23, 2003)

Video Transmission System Equipment

Video transmission system equipment shall be manufactured by Communication Specialties, Inc.

1.	Equipment Model Numbers:

10-channel digital video transmitter	Pure Digital Fiberlink

3132-F-9

10-channel digital video receiver	Pure Digital Fiberlink

3133-F-9

2.	Manufacturer Information:

Communication Specialties, Inc.

55 Cabot Court

Hauppauge, NY 11788

Telephone: (631) 273-0404

Fax: (631) 273-1638

www.commspecial.com

info@commspecial.com

8-20.2.OPT19(J).ITS.DT1

(NWR ITS October 21, 2003)

Video and Data Transmission System Equipment

Video and data transmission system equipment shall be manufactured by Communication Specialties, Inc.

1.	Equipment Model Numbers:

10-channel digital video transmitter	Pure Digital Fiberlink 3332-F-9

10-channel digital video receiver 	Pure Digital Fiberlink 3333-F-9

2.	Manufacturer Information:

Communication Specialties, Inc.

55 Cabot Court

Hauppauge, NY 11788

Telephone: (631) 273-0404

Fax: (631) 273-1638

www.commspecial.com

info@commspecial.com

8-20.2.OPT19(K).ITS.DT1

(NWR ITS September 26, 2005)

EIA -422 Combiner Unit

The Contractor shall provide and install the EIA-422, 4-wire combiner as shown in the Plans.  The combiner shall be manufactured by Vicon, Inc.  The Contractor shall provide and install cables from the combiner to the Video/data receivers.  The combiner shall have one master port and 10 output ports:

1.	Equipment Model Numbers:

Combiner: Model V1400X-IDL Intelligent Distribution Line Control

2.	Manufacturer Information:

Vicon Industries, Inc.

89 Arkay Drive

Hauppauge, NY  11788

Telephone: (800) 645-9116

or (631) 952-2288

www.vicon-cctv.com

8-20.2.OPT19(L).ITS.DT1

(NWR ITS October 23, 2006)

EIA –232 Data Broadcast Unit

The Contractor shall provide and install a rack-mounted EIA-232 data broadcast unit. The data broadcast unit shall be manufactured by Black Box, Inc. The broadcast unit shall have one master port and 8 output ports:

1.	Equipment Model Numbers:

8-Line Broadcast data broadcast unit	TL158A-R4

Rack-mount bracket	TL486

2.	Manufacturer:

Black Box, Inc.

1000 Park Dr

Lawrence, PA 15055-1018

Telephone:  (877) 877-2269

www.blackbox.com

e-mail: info@blackbox.com

8-20.2.OPT19(M).ITS.DT1

(NWR ITS February 23, 2009)

Rack-mounted Color Monitor

The monitor shall be a color video monitor with a 13” or 14” diagonal picture LCD. The monitor shall support EIA NTSC standard color composite video signals (1.0 V p-p, 75 Ohm) and have a resolution of at least 400 horizontal lines. The monitor shall include a minimum of two video input ports; one shall be BNC-type for composite video and one shall be 4-pin (Y/C) type for S-Video. The video output port shall be BNC-type for composite video. The monitor shall include a rear panel slide switch that enables video termination of Hi-Z or 75 ohm.

The monitor’s power source shall be 120 VAC +/- 10%, 60Hz.

The monitor dimensions shall not exceed 14”(H) by 18”(D). The monitor shall have a metal casing and be factory-equipped with rack-mounting hardware (EIA 19”). The monitor weight shall not exceed 40 lb.

The Contractor shall supply one BNC coaxial patch cord (RG-59U) of sufficient length to connect the monitor to all video sources mounted in the rack.

The monitor shall be manufactured by Sony, JVC, or Philips

8-20.2.OPT19(N).ITS.DT1

(NWR ITS February 23, 2009)

SONET Network Element

The Contractor shall install and connect SONET network elements as shown in the Plans to provide voice and data communications over fiber optic cable.  The network elements shall provide OC-48 service. The network element shall be capable of providing local interface for Gigabit Ethernet, 10/100 Ethernet and T-1 services. The SONET network elements shall be manufactured by Cisco Systems, Inc.

1.	Equipment Model Numbers:

| Description | Part Number | Qty |
| --- | --- | --- |
| 15454 ATO (Assemble to Order) | CISCO15454 | 1 |
| 15454 Network Element shelf with ship kit | 15454-SA-HD | 1 |
| 15454 Shelf Fan Tray Assembly, HPCFM, I-Temp | 15454-FTA3-T | 1 |
| Alarm Interface Controller Card, I-Temp | 15454-AIC-I | 1 |
| Electrical Interface Panel (A-side) | 15454-EIA-1AMPA84 | 1 |
| Timing, Communications, and Control v2-plus Card, I-Temp, SONET | 15454-TCC2P-K9= | 2 |
| System Software, Pre-loaded on TCC (Current Release) | SF15454-R(Cur.Rel.)K9 | 2 |
| Cross-connect Card, 1152 STS, 672 VT | 15454-XC-VXC-10G | 2 |
| Cable Assembly, AMP/champ to wire-wrap (15 ft). | 15454-AMP-WW-15= | 1 |
| DS1 Card, I-Temp | 15454-DS1-14 | 1 |
| DS1:N Protection Card, I-Temp | 15454-DS1N-14 | 1 |
| 12-port 10/100BaseT Ethernet Card | 15454-ML100T-12 | 1 |
| Gigabit Ethernet Card with 2 GBIC Slots | 15454-ML1000-2 | 1 |
| GBIC - 1000Base-SX, MM, SC connectors | ONS-SC-GE-SX= | 2 |
| Long Range OC-48 Card, 1550, 1 Ckt., SC connectors | 15454-MRC-2.5G4 | 2 |
| SFP - OC48, LR, 1550, I-Temp | ONS-SI-2G-L2 | 4 |
| Empty slot Filler Panel | 15454-BLANK | 6 |
| Feature Pkg. CD, Right to Use License, 15454 (Current Release) | 15454-R(Cur.Rel.)SWK9 | 1 |
| System Documentation, English, CD (Current Release) | 15454-DOC(Cur.Rel.)CD | 1 |

2.	Manufacturer Information:

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134

Telephone: (408) 526-4000

www.cisco.com

Local Contact:

Mr. Fred Fox

Optical Products Specialist

500 108th N.E. Suite 500

Bellevue, WA 98004

8-20.2.OPT19(O).ITS.DT1

(NWR ITS September 26, 2005)

Fuse Panel

The Contractor shall provide, install and connect a fuse panel as shown in the Plans.  The fuse panel shall be manufactured by Comm/net Systems, Inc.

1.	Equipment Model Numbers:

KTK Fuse/Alarm Panel 	016-105-10

KTK Fuse, 10 Amp	KTK-10

KTK Fuse, 30 Amp.	KTK-30

2.	Manufacturer Information:

Communications Network (Comm/net) Systems, Inc.

4237 24th Ave. W.

Seattle, WA 98199

Telephone: (206) 282-8670

8-20.2.OPT19(P).ITS.DT1

(NWR ITS September 26, 2005)

Cross-Connect Panel

The Contractor shall provide and install digital cross-connect panels as shown in the Plans. The Cross-connect panels shall be used to connect and terminate DSX circuits from the SONET equipment. The cross-connect panels shall be manufactured by ADC Telecommunications, Inc.

1.	Equipment Model Numbers:

DSX1 Shelf, 19”	PX1-B00004

DSX1 Octapak housing	PIX-1C-OCT

DSX1 Circuit Card	PIX-1C

2.	Manufacturer Information:

ADC Telecommunications, Inc.

4900 West 78th Street

Minneapolis, MN 55435

Telephone: (800) 366-3891

www.adc.com

8-20.2.OPT19(Q).ITS.docx

(******)

Contact Closure Over Ethernet (COE)

The Contractor shall provide and install contact Closure Over Ethernet (COE) equipment as shown in the Plans.

1.	Equipment Model Numbers:

COE Digital I/0  		ioLogik E1214

### DIN Rail Power Supply	MDR-40-24

2.	Manufacturer Information:

Moxa Americas

601 Valencia Avenue, #100

Brea, California 92823

Toll-free: 1-888-669-2872

Tel: +1-714-528-6777

Fax: +1-714-528-6778

www.moxa.com

8-20.2.OPT19(R).ITS.docx

(******)

Video Decoder

The Contractor shall provide and install two video decoders in the Dayton Avenue Traffic Management Center (TMC).

1. Equipment Model Number:

1-port video decoder (standalone)		CohuHD Series 9710HD

Model 9712-2000

2. Manufacturer Information:

CohuHD

12367 Crosthwaite Circle

Poway, CA 92064-1245

Telephone: (858)-391-1800

www.cohuHD.com

8-20.2.OPT46.ITS.DT1

(NWR ITS February 23, 2009)

Communication Hub / Concrete Universal Enclosure (CUE)

The concrete universal enclosure shall be supplied by Emerson Network Power.

1.	Equipment Model Numbers:

Concrete Universal Enclosure	CUE-610 (F2007097)

2. 	Manufacturer Information:

Emerson Network Power

ATTN: Mr. Scott Hein

4350 Weaver Parkway

Warrenville, IL  60555

Telephone: (630) 579-5256

http://www.emersonnetworkpower.com/energysystems/

General

The enclosure shall function as an unattended facility with a controlled-environment suitable for the installation of the system equipment and regular, safe inspection and maintenance by operating personnel.  Appropriate electrical, mechanical, and environmental systems shall be provided to support the specific equipment installation.

Enclosure Description

The enclosure shall be a manufactured concrete enclosure, intended for partial underground installation.  The structure shall be manufactured of 5000PSI steel-reinforced pre-cast concrete with a heavy gauge metal door and cable rearrangement facility (CRF).

Personnel access shall be through an entrance door that shall be the only access to the enclosure interior.  A vertical ladder shall be provided within the entranceway. The entry size shall be nominally 56.5 inches high x 28 inches wide and provide a clear entry area for system equipment components that are field installed.  The entrance shall include a heavy-duty locking mechanism controlled by a keyed cylinder lock set for security.

The lock mechanism shall be a Best Lock Company 7-pin CX series, manually operable from within (to avoid entrapment) and key operable from the exterior.  The exterior lock cylinder shall be installed in a manner to provide for protection from the weather.  The Contractor shall supply green construction cores. Upon substantial completion, the Contractor shall deliver two master keys and one core removal key to the Engineer. The entry door shall be equipped with a wind latch to avoid accidental closure.

Any water leakage into the enclosure could disrupt the system equipment operation. Therefore, the enclosure design shall minimize any leakage potential, and as an added measure, provide for containment of water in a below-floor sump area.  Water containment capacity and monitoring shall be sufficient to provide adequate warning (under normal circumstances) to permit the dispatch of personnel to investigate any problem.

Cable entry and/or exit are to be provided as four (4), 4-inch diameter openings into the cable rearrangement facility (CRF) cabinet at the rear of the enclosure. No outside plant cable shall be brought into the enclosure. No metallic conduit connections to field conduits shall be permitted. Power shall be supplied to the enclosure via a 2.5-inch port in the power transfer switch cabinet located on the exterior of the enclosure.

An overhead cable ladder rack and a fiber management system shall be supplied with the enclosure.

The enclosure shall include a fold-up work table attached to the wall as shown in the plans.  Nominal dimensions of the table shall be 3 feet wide by 2 feet deep.

The enclosure shall be complete with the necessary electrical and environmental equipment preinstalled to provide a safe, controlled environment suitable for personnel and the electronic system.

Enclosure Environmental System

An Environmental Control Panel (ECP) shall be provided to monitor all environmental conditions within the enclosure and shall control respective equipment to maintain or correct the condition(s) that exist.  This panel shall also provide contacts for remote alarm indications.

The enclosure shall be equipped with dual 12000 BTU air conditioners to maintain proper temperature levels.

The enclosure environmental system shall be capable of maintaining a controlled environment including the maintenance of interior temperatures within a nominal range of between 40( F and 90( F.

An atmospheric monitor shall be provided with the ECP to continuously sample the air with the enclosure.  The monitor functions and remote alarms are described in a following section of this specification.

An immediate visual indication of a safe or hazardous enclosure atmosphere shall be provided by green and red pilot lights visible through the open entrance door. Audible alarms shall supplement the visual indication during potentially hazardous conditions.  Safe conditions shall be indicated with a continuous green light.  Unsafe conditions shall be indicated with a continuous red light and audible alarm horn.  In addition, an unsafe atmospheric condition shall activate the ventilation system to purge the enclosure chamber and initiate a remote alarm.

A sump pump shall be provided as part of the CUE. The pump shall be mounted in a sump pit to which water is channeled via a trough around the floor perimeter.  The pump shall activate alarms upon activation of the float switch.

Enclosure Security/Monitor Alarms

Alarm indications shall be wired to an Alarm Terminal Block (ATB) so the existence of any alarm condition can be transmitted to a remote location.  The alarm indications shall be given as a dry, normally open contact closure.  No indication of remote (silent), dry contact alarms need be provided at the enclosure; however, hazardous alarm conditions shall provide audible or visual alarm indications at the enclosure when occupied for personnel safety.  No audible alarm should be heard when the enclosure is unoccupied; however, the remote alarm shall continue to function.  Upon opening the entry door, any pre-existing hazardous condition shall immediately trigger the local alarms.

The Contractor shall provide all necessary equipment and wiring to connect the above alarms to the Administrative, Operations, Maintenance facilities of the SONET system so as to provide a functioning alarm system from the Communication Hub to the TSMC at Dayton.

The following alarms shall be provided for:

Intrusion Alarm

A remote alarm indication shall be activated immediately upon opening the entrance door. Closing the entrance door shall restore the alarm switch to its normal position.

Water Detection Alarm

A water sensor located approximately 8 inches below floor level shall signal a remote alarm condition if water is present at the sensor.  The sensor shall detect water film depth as little as 1/16 inch.  This shall provide an early alarm for a cable duct leak or other water leakage that could damage the system equipment and the enclosure interior if the condition is not corrected.

Sump Pump Run Alarm

The ECP shall monitor the sump pump operation and provide a remote alarm indication if the pump  is running.

High Water Alarm

A float switch shall monitor water level and initiate a final water alarm in the event of a rise in water level beyond the capability of the sump pump. This alarm point shall occur at least 4 inches below the floor level were equipment is installed.

Explosive Atmosphere Alarm

An alarm indication shall be activated by an unsafe condition reported by the Atmospheric Monitor explosive-gas sensing element.  Explosive gas is defined as 10% or more lower explosive level (LEL) of Methane.  Detection of explosive gas shall:

(1)	initiate a remote alarm,

(2)	give an immediate, steady red pilot light indication in the entrance way,

(3)	activate the fresh air blower,

(4)	sound a local alarm.

The remote alarm shall provide an immediate remote alarm indication, even though the fresh air blower may clear the explosive condition.  Additionally, the local audible alarm and red pilot light shall be activated for immediate indication of a hazardous condition.  It shall not be possible to silence the local audible alarm at the enclosure, and the red pilot light shall remain lighted until the condition clears.  Once the Atmospheric Monitor reports a safe condition, these alarms and indications shall be automatically deactivated.

Toxic Atmosphere Alarm

An alarm indication shall be activated by an unsafe condition reported by the Atmospheric Monitor toxic gas sensing element.  Toxic gas (100 parts/million Carbon Monoxide) detection shall:

(1)	initiate a remote alarm,

(2)	give an immediate, steady red pilot light indication in the entrance way,

(3)	activate the fresh air blower,

(4)	sound a local alarm.

The delayed remote alarm shall provide an opportunity for the fresh air blower to clear the toxic condition before reporting the condition remotely. Locally, however, the audible alarm and red pilot light shall be activated for immediate indication of a hazardous condition.  It shall not be possible to silence the local audible alarm at the enclosure and the red pilot light shall remain lighted until the condition clears.  Once the Atmospheric Monitor reports a safe condition, these alarms and indications shall be automatically deactivated.

Smoke Alarm

The atmospheric monitor shall incorporate a photoelectric smoke detector. Upon detection the system shall:

(1)	initiate a remote alarm,

(2)	give an immediate, steady red pilot light indication in the entrance way,

(3)	deactivate and lock out the fresh air blower,

(4)	sound a local alarm.

The audible alarm and red pilot light shall be activated for immediate indication of a hazardous condition.  It shall not be possible to silence the local audible alarm at the enclosure and the red pivot light shall remain lighted until the condition clears.  Once the Atmospheric Monitor reports a safe condition, these alarms and indications shall be automatically deactivated.

Atmospheric Monitor Failure Alarm

The atmospheric monitor shall initiate a remote alarm condition upon:

(1)	failure of any gas sensor,

(2)	failure of AC and DC backup power sources.

High Humidity Alarm

An alarm humidistat shall be provided at the ECP to give a remote alarm indication if the relative humidity (RH) reaches a preset level.  The High Humidity alarm point shall be adjustable between 20% and 80% RH.

High Temperature Alarm

An alarm thermostat shall be provided at the ECP to give a remote alarm indication if the enclosure interior temperature exceeds a preset level.  The High Temperature alarm point shall be selectable in a range from 55 to 175 degrees Fahrenheit.  The alarm shall activate when the temperature in the CUE reaches 110( F, and reset at 90( F.

Power Failure Alarm

An interruption of the Utility Service shall cause a remote alarm indication. Restoration of power shall silence the alarm.  Both legs of the 120/240V single-phase service shall be monitored so a failure of either one or both legs shall trigger the alarm condition.

Power Transfer Switch

The enclosure shall be equipped with an automatic Power Transfer Switch (PTS) to allow connection of an external generator in the event of an extended power outage. The PTS shall be located on the outside of the enclosure next to the entrance door and shall be equipped with a connecting plug suitable for use with existing State owned ONAN generators, and shall be able to communicate with the State owned generators

PTS Equipment Model Numbers:

Transfer Switch-Power Command: 40A/70A/125A

OTPC125	Automatic Transfer Switch-Onan, PwrCmd, 125 Amp

A028-7	Poles – 3

A035-7	Application - Utility To Genset

A046-7	Listing – UL 1008/CSA Certification

A044-7	Frequency – 60 Hertz

A041-7	System – Single Phase, 2 wire or 3 wire

R023-7	Voltage – 240 VAC

B002-7	Cabinet – Type 3 (outdoor)

C023-7	Control – Transfer Switch, Level 1

N020-7	Terminal Block – Retransfer Inhibit

G002-7	Transfer Switch Warranty – 1 year basic

CP01-7	Common parts listing

SPEC-A	Product revision – A

C024-7	Switch control – Level 2

M017	Security key – Front panel

M018	Display – Digital

Generator Plug: Appleton Model ADR1034RS with AJA-100 Adaptor

Uninterruptible Power Supply (UPS)

A 3KVA rack-mounted UPS with extended battery packs shall be installed in the 23” UPS rack. The battery packs shall be installed midway in this rack followed by the UPS and External maintenance bypass switch.

The UPS shall be an Alpha Technologies Pinnacle 016-313-10 equipped with three (3) extended battery pack part numbers 016-315-10.  The UPS system shall be connected to a dedicated power circuit hardwired from the hub circuit breaker panel. The output of the UPS system shall be hardwired to a wall-mount circuit breaker panel to provide UPS power to outlets mounted on the walls behind the equipment racks and next to the fold down table.  Alarm contact outputs from the UPS alarm output terminations shall be wired using Category 3 cable to the appropriate terminal block location in the hub to be specified by the engineer.

A maintenance bypass switch (MBS) shall be provided and installed in the UPS rack directly above the UPS. The MBS shall allow a dedicated circuit from the hub circuit breaker panel to feed the utility bypass input of the MBS and from the MBS output to the UPS wall mount circuit breaker panel that feeds the outlets behind the equipment racks.

Equipment Model Numbers:

UPS: Alpha Technologies Pinnacle PIN 3000RM

Extended Battery Pack: PBP36-0706U2R

DC Power System

A rack-mounted –48 volt DC power system shall be provided as part of the CUE.  The DC power system shall operate separately from the UPS system and shall be used to power all –48VDC equipment.

The DC power system shall consist of a modular dual rectifier, low voltage disconnect module, control panel and battery pack capable of powering the Voice and Data Transmission equipment. The output of the rectifiers shall be adjustable by front panel control. A front panel mounted display shall be provided as part of the power supply.

A battery supply and mounting tray shall be provided. Batteries shall be mounted in the lower part of the rack with the rectifier system installed above.

Equipment Model Numbers:

Rectifier System: Emerson VMS-75

With 2 ea VF15F50 Power conversion unit, 1 ea DC Distribution module and 1 ea Meter-Control module

Battery Pack: 12AVR100-3ET (Includes Tray and Harness)

8-20.2(9-29.2(2)A).GR8

Standard Duty Cable Vaults and Pull Boxes

Section 9-29.2(2)A is supplemented with the following:

8-20.2(9-29.2(1)A).OPT1.GR8

(August 1, 2016)

Concrete Junction Boxes

Both the slip-resistant lid and slip-resistant frame shall be treated with Mebac#1 as manufactured by IKG industries, or SlipNOT Grade 3-coarse as manufactured by W.S. Molnar Co. Where the exposed portion of the frame is ½ inch wide or less the slip-resistant treatment may be omitted on that portion of the frame. The slip-resistant lid shall be identified with permanent marking on the underside indicating the type of surface treatment (“M1” for Mebac#1; or “S3” for SlipNOT Grade 3-coarse) and the year manufactured.  The permanent marking shall be 1∕8 inch line thickness formed with a mild steel weld bead.

8-20.2(9-29.2(4)).DT1

Cover Markings

8-20.2(9-29.2(4)).INST1.ESP.DT1

Section 9-29.2(4) is supplemented with the following:

8-20.2(9-29.2(4)).OPT1.ESP.DT1

(NWR February 11, 2013)

Junction Box Identification

Junction boxes shall be marked “WSDOT” when the junction boxes are to be installed as part of a future raceway system in a bridge structure, vehicle barrier, pedestrian barrier, or roadway crossing and the future raceway system is not connected to an illumination, signal, interconnect, or ITS raceway system.

Junction boxes, pull boxes and cable vaults containing only Traffic Signal Interconnect (fiber optics) cable shall be marked or embossed with the legend “COMM”.

8-20.2(9-29.3).ITS.DT1

Fiber Optic Cable, Electrical Conductors, and Cable

Section 9-29.3 is supplemented with the following:

8-20.2(9-29.3(1).ITS.DT1

Fiber Optic Cable

Section 9-29.3(1) is supplemented with the following:

8-20.2(9-29.3).OPT1.ITS.DT1

(NWR ITS April 10, 2006)

Communication Cables And Interfaces

Quality Assurance

All materials described in this section shall meet or exceed the applicable provisions of the following documents:

1.	CFR Title 7, Section 1755.900, RUS Specification for Filled Fiber Optic Cables

2.	ANSI, C8.47-1983, American National Standard for Polyolefin-insulated Thermoplastic Jacketed Communication Cables

3.	TIA/EIA-455-28-C, Method for Measuring Tensile Failure Point of Optical Waveguide Fibers

4.	TIA/ElA-455-34-A, Interconnection Device Insertion Loss Test

5.	TIA/EIA-455-95-A, Absolute Optical Power Test for Optical Fibers and Cables

6.	EIA-598-B, Color Standard for Optical Fibers

8-20.2(9-29.3(1)).OPT1.ITS.docx

(******)

Fiber Optic Cables

The Contractor shall provide manufacturer's certification that the submitted cable shall comply with the Rural Utilities Service (RUS) Specification 1755.900 as currently amended and with the requirements set forth in this Special Provision.  Any deviations from these specifications shall be conspicuously noted in the Contractor's submittal.

Each cable shall contain the total number of optical fibers as specified in the Plans. The fibers shall be placed in loose buffer tubes in groups of 12.  .

The fiber optic cable outer jacket shall be marked with the manufacturer’s name, the year of manufacture, the words OPTICAL CABLE and sequential meter marks.  The markings shall be repeated every one meter.  The actual length of the cable shall be within +/- 0.1% of the length marking.  The marking shall be in contrasting color to the jacket.  The marking shall be 2.5mm in height and shall be permanent and weatherproof.

Cable shall be of loose tube design.  The tubes shall be surrounded by dry moisture blocking filling compound or tape.  The tubes may be filled with dry moisture blocking powder surrounding the fibers.

The cable shall be constructed with the following components:

1.	A dielectric central strength member

2.	Buffer tubes containing optical fibers

3.	Aramid (Kevlar) yarn

4.	Outer MDPE jacket

The Contractor shall provide all materials required for the installation and splicing of the specified communications cables, power cables and associated interface devices.

The Contractor shall provide an unconditional warranty on all installed cable for a period of one (1) year.

At the request of the Engineer, the Contractor shall submit a 3-foot sample cable section to the Engineer for approval for each type of cable to be provided.

8-20.2(9-29.3(1)A).ITS.DT1

Singlemode Fiber Optic Cable

Section 9-29.3(1)A is supplemented with the following:

8-20.2(9-29.3(1)A).OPT1.ITS.DT1

(NWR ITS October 31, 2005)

Communication Cables And Interfaces

Optical fiber shall meet the requirements of ITU G652 and specifically meet ITU G652.D Attributes.  The fibers shall support the transmission of wavelengths for Coarse Wavelength Division Multiplexing (CWDM) as defined in ITU G694.2.

8-20.2(9-29.3(1)A).OPT2.ITS.DT1

(February ITS 11, 2002)

Communication Cables And Interfaces

Multimode Optical Fibers

All multimode  optical fiber cable  shall be of a loose tube buffer design and of industry standard construction for underground conduit installations as well as of an all dielectric construction.

Each optical fiber shall be fabricated from 100 K PSI glass and shall meet this specification.

The multimode fibers shall have a nominal core diameter of 62.5 microns, with no variation greater than 3 microns.  The non circularity of the core surface shall be less than 6 percent.  Core non circularity is defined as the difference between the longest and shortest chords each passing through the center of the core and connecting on the core/cladding interface, divided by the average core diameter.  Optical fiber dimensions shall be in compliance with the methods for measuring as established in EIA-STD, 455-176.

The multimode cladding shall have a nominal outside diameter of 125 microns with no variation greater than 3 microns.  Non circularity of the cladding surface shall be less than 4 percent.  Cladding non circularity is defined as the difference between the longest and shortest chords, each passing through the center of the cladding and connecting points on the outer cladding surface, divided by the average diameter of the cladding surface.

The concentricity error for multimode optical fibers shall be less than 6 percent, where the error is the distance between the core and cladding centers divided by the average core diameter.

The coated multimode optical fibers shall have a nominal outside diameter of 250 microns, with no variation greater than 15 microns and a minimum coating thickness of 50 microns.

Fibers shall contain no factory splices.

The maximum attenuation of each 62.5/125 multimode fiber at the temperature range of -40(C. to +70(C. shall be no greater than 1.00 dB/km at 1310 nm nominal.  The information transmission capacity (bandwidth) for each multimode optical fiber shall be 500 MHz-km.  The attenuation shall be measured on a completed reel length of cable then normalized to a length of 1 km.  The measurement method shall be in accordance with the manufacturer's recommended procedure.

All fibers shall be free from imperfections and inclusions that would prevent them from meeting the transmission and mechanical requirements of this specification.  Anomalies shall not exceed 0.20 dB.

The maximum dispersion at 68(F. shall be 2.6 ps/nm-km over the range of 1225 to 1330 nm.

The cutoff wavelength shall be 1200 nm nominal, and shall have no variation greater than 70 microns.

Optical Performance

The optical performance shall meet the requirements of the specifications.

Contractor shall warrant that the installed cable shall provide an absolute maximum attenuation of no greater than 3.0 dB/km at 850 nm nominal and 1.0 dB at 1300 nm nominal for each 62.5/125 multimode fiber at the temperature range of -40(C. to +70(C.  The attenuation of multimode fibers shall be determined by EIA-STD-455-46.

The information transmission capacity (bandwidth) of each multimode optical fiber shall be 500 MHz_km.  The information capacity of each fiber shall be measured in the time domain environment and the result shall be expressed in terms of _3 dB (optical power) frequency.  The method to determine the pulse distortion shall be EIA,-STD-455-51.

8-20.2(9-29.3(2)).ITS.DT1

Twisted Pair Communication Cable

Section 9-29.3(2) is supplemented with the following:

8-20.2(9-29.3(2)).OPT1.ITS.DT1

(NWR ITS September 26, 2005)

Communication Cables And Interfaces

The twisted pair cable outer jacket shall be marked with the manufacturer’s name, the year of manufacture, and sequential meter marks.  The markings shall be repeated every one meter.  The actual length of the cable shall be within +/- 0.1% of the length marking.  The marking shall be in contrasting color to the jacket.  The marking shall be 2.5mm in height and shall be permanent and weatherproof.

8-20.2(9-29.3(2)).OPT2.ITS.docx

(******)

Outdoor Rated Category 6 Cable

A Category 6 outside plant rated cable shall be provided for connecting Ethernet devices that are in separate cabinets. The cable shall contain four twisted pairs of #23 or 24AWG solid bare copper wire. Each pair shall be uniquely color coded with a Thermoplastic polyolefin jacket.

The cable outer jacket shall be Polyolefin with a minimum wall thickness of 0.040”. The cable shall be flooded for moisture protection.

The cable shall have a voltage rating of 300V.

The cable shall be UL listed. It shall support up to IEEE 802.3 1000Base‐T Ethernet and IEEE 802.3af for power over Ethernet.

The cable shall be terminated on each end with an RJ45 connector.

8-20.2(9-29.13).ITS.DT1

Traffic Signal Controllers

Section 9-29.13 is supplemented with the following:

8-20.2(9-29.13).OPT1.ITS.DT1

Traffic Data Accumulation And Ramp Metering System

8-20.2(9-29.13).OPT1(A).ITS.DT1

(NWR ITS February 23, 2009)

Model 170E Controller

Each ramp meter and data station controller unit furnished shall meet the requirements specified in Chapter 2 of the Caltrans Transportation Electrical Equipment Specification (TEES), August 2002, as currently amended and modified as follows:

1.	The 170E CPU module shall operate a 68HC11F1 MPU at a crystal frequency of 8MHz.  The MPU shall be socket mounted in a PLCC socket.

2.	The EPROM shall be resident on the CPU module.  The EPROM socket shall be a 32-pin lever-controlled ZIF device.  The EPROM shall be either a 32K x 8 or a 128K x 8 device.  The device size shall be jumper selectable.

3.	Feature and Location switches shall be provided on the front portion of the CPU module.  Each switch shall be an 8-position front-reading DIP switch.  The switches shall be addressed as follows:

Location Switch at 7000 (Port A)

Feature Switch at 700A (Port E)

4.	There shall be one LED indicator located on the front of the CPU module.  This LED shall be connected to bit 3 of Port G.

5.	The 170E controller shall have a minimum of 28 kB of battery backed static RAM on the CPU module.  RAM shall be continuous from location 0000 to 6FFF.

6.	Four Asynchronous Communication Interface Adapters (ACIAs) shall be provided on the same board as the CPU.  The ACIAs shall be 6850 ICs operating at a crystal frequency of 6.144MHz.  Each ACIA shall have 5 programmable jumpers to select 5 communication baud rates (1200, 2400, 4800, 9600, 19200) for a total of 20 jumpers.  All ACIAs shall be active.  An IRQ status register shall be provided at75FF.

7.	The Model 412C PROM module shall not be provided.  A blank panel shall cover the PROM slot.

8.	Two blank 27256 EPROM chips shall be provided with the CPU module.

9.	Each controller shall have an ACIA C20 wrap-around with the following pin connections:

C20 Function Pin	C20 Function Pin

(J) RTS	to	(M) CTS
(J) RTS	to	(H) DCD
(K) DATA-IN	to	(L) DATA-OUT

8-20.2(9-29.13).OPT1(A)3.ITS.DT1

(NWR ITS February 23, 2009)

10.	Each 170E controller shall include an unmanaged ethernet switch and a cabinet device server.

8-20.2(9-29.13).OPT1(C).ITS.DT1

(NWR ITS October 4, 2004)

Model 334 Cabinet

Traffic data station and ramp meter controller cabinets furnished on this contract shall meet the requirements of Type 170E, 170E-HC-11, 2070, 2070 Lite, ATC Controller Cabinets.

8-20.2(9-29.13).OPT1(C)1.ITS.docx

(******)

Model 334L Cabinet

The cabinet shall meet the requirements of section 9-29.13(11) Traffic Data Accumulation and Ramp Meters.

Section 9-29.13(11) is supplemented with the following:

One rack mount vehicle loop detector shall be included for every two loops.  Five additional vehicle loop detectors shall be installed in each new cabinet for future use.

One reproducible drafting film and two non-fading copies of the cabinet-wiring diagram shall be furnished with each cabinet.

Cabinet Wiring

Cabinet wiring shall conform to the details and diagrams in the Plans.  The Contractor shall trim wiring to eliminate all slack and lace or bind together with nylon wraps or equal.  All terminals shall be labeled.  The cabinet shall be wired completely so that the only requirement to make a field location completely operational is to connect field, power and ground wires to appropriate terminals.

8-20.2(9-29.13).OPT1(D).ITS.DT1

(NWR ITS October 4, 2004)

Rack Mount Vehicle Loop Detectors

The Contractor shall provide, install and connect inductive loop detectors manufactured by Reno A&E.

1.	Equipment Model Numbers:

332/170 type with solid-state outputs 	C-1101-SS

and TrueCount outputs

2.	Manufacturer Information:

Reno A&E

4655 Aircenter Circle

Reno, NV  89502

Telephone: (775) 826-2020

www.renoae.com

8-20.2(9-29.13).OPT1(E).ITS.DT1

(NWR ITS February 23, 2009)

Rack Mount Vehicle Loop Detectors in Existing Cabinets

The Contractor shall provide, install and connect inductive loop detectors manufactured by Reno A&E in all existing cabinets that have new loops installed or existing loops replaced.  One rack mount vehicle loop detector shall be included for EACH new loop installed or replaced.

1.	Equipment Model Numbers:

332/170 type with solid-state outputs 	C-1101-SS

and TrueCount outputs

2.	Manufacturer Information:

Reno A&E

4655 Aircenter Circle

Reno, NV  89502

Telephone: (775) 826-2020

www.renoae.com

8-20.2(9-29.13).OPT1(F).ITS.docx

(******)

Non-Intrusive Vehicle Detector

The Contractor shall provide, install, and connect non-intrusive vehicle detector units in locations as shown in the Plans. The Non-Intrusive Vehicle Detector shall be manufactured by Wavetronix LLC as a completed unit including detector sensor, cable, mounting brackets, and other associated equipment.

1.	Equipment Model Numbers:

| Wavetronix SmartSensor HD | WX-101-0415 |
| --- | --- |
| SmartSensor Mount | WX-SS-611 |
| Click 112 - Contact Closure Card | WX-CLK-112 |
| Click 201 - Power Supply | WX-CLK-201 |
| Click 200 - Surge Suppressor | WX-CLK-200 |
| Click 304 – RS-232 to RS-485 Converter | WX-CLK-304 |
| SmartSensor 8c Cable | WX-SS-706-040 |
| Sensor 8c Home Run Cable | ATP-Matrix 2 or WX-SS-707-xx |
| Click 210 – AC Circuit Breaker | WX-CLK-210/02 |
| Click 230 – 120 VAC Surge Protector | WX-CLK-230 |

2.	Manufacturer Information:

Wavetronix LLC

380 S. Technology Ct.

Linden, UT 84042

(801) 764-0277 (ext. 1011)

www.wavetronix.com

8-20.2(9-29.13).OPT1(G).ITS.DT1

(NWR ITS November 10, 2003)

Traffic Signal Standards

Ramp meter signal standards shall meet the requirements of Standard Plan J-7a.

8-20.2(9-29.13).OPT1(H).ITS.docx

(******)

Model 334D/C Traffic Data Accumulator and Camera Cabinet

All cabinets designated for use as a model 334D/C traffic data accumulator and camera cabinet shall be Type 334L cabinets furnished to meet the TEES  with the modifications listed in Section 9-29.13(10)D and  include the following accessories:

1.	Each cabinet shall be equipped with a fully operable controller equipped as specified in the Contract Provisions.

2.	One input file, shall be provided.

3.	The PDA #3L shall include a model 206L power supply. Load switches, second relay, and model 208 Monitor Unit are not required.

4.	 A plug mold strip mounted on the side panel with a minimum of 8 individual outlets.

5.	Display Panel

A.	General

Each cabinet shall be furnished with a display panel. The panel shall be mounted, showing and providing detection for inputs and specified controller outputs, at the top of the front rack above the controller unit. The display panel shall be fabricated from brushed aluminum and constructed according to the detail in the Plans.

B.	Text

All text on the detector panel shall be black in color and silk screened directly to the panel except the Phenolic detector and cabinet nameplates.

A nameplate for each loop shall be engraved with a ¼-inch nominal text according to the ITS Field Wiring Charts. The nameplates shall be permanently affixed to the detector panel.

C.	LEDs

The LEDs for the display panel shall meet the following Specifications:

Case size	T 1-¾

Viewing angle	50° minimum

Brightness	50 Milli candelas minimum

LEDs with RED, YELLOW or GREEN as part of their labels shall be red, yellow or green in color. All other LEDs shall be red. All LEDs shall have tinted diffused lenses.

D.	Detector panel Control Switch

Each display panel shall be equipped with one detector display control switch on the panel with labels and functions as follows:

ON

Detector panel LEDs shall operate consistent with their separate switches.

OFF

All detector indicator LEDs shall be de-energized. Detector calls shall continue to reach the controller.

TEST

All detector indicator LEDs shall illuminate and no calls shall be placed to the controller.

E.	Detector Input Indicators

One LED and one spring-loaded two-position SPST toggle switch shall be provided for each of the 28 detection inputs. These LEDs and switches shall function as follows:

TEST

When the switch is in the test position, a call shall be placed to the controller and energize the associated LED. The switch shall automatically return to the run position when it is released.

RUN

In the run position the LEDs shall illuminate for the duration of each call to the controller.

F.	Connectors

Connection to the display panel shall be made by three connectors, one pin (labeled P2) and one socket (labeled P1) and one labeled C5. The P1 and P2 connectors shall be 50-pin cannon D series, or equivalent 50 pin connectors and shall be compatible such that the two connectors can be connected directly to one another to bypass the input detection. Wiring for the P1, P2 and C5 connectors shall be as shown in the Plans.

The Contractor shall install wire connectors P1, P2, C1P, C2, C4, C5 and C6 according to the pin assignments shown in the Plans.

6.	Police Panel

No toggle switch shall be installed.

7.	Fiber Optic Patch Panel

The Contractor shall provide and install a rack-mounted fiber optic patch panel as identified in the Plans.

8.	Camera Terminal Block

Each cabinet shall house one termination block for termination of each camera control cable, the optical transmitter, and the camera control receiver.  These cables shall be identified and marked by the Contractor.

Cabinet Wiring

Terminal blocks TB1 through TB6 shall be installed on the Input Panel. Layout and position assignment of the terminal blocks shall be as noted in the Plans.

Terminals for field wiring in traffic data cabinet shall be labeled.

Loop lead-in cables shall be labeled and connected to cabinet terminals according to the ITS Field Wiring Chart. This chart will be provided by the Engineer within 20 days of the Contractor’s request.

8-20.2(9-29.13(11)).ITS.DT1

Traffic Data Accumulator and Ramp Meters

Section 9-29.13(11) is supplemented with the following:

8-20.2(9-29.13(11)).OPT1.ITS.docx

(******)

One rack mount vehicle loop detector shall be included for every two loops.  Five additional vehicle loop detectors shall be installed in each new cabinet for future use.

One reproducible drafting film and two non-fading copies of the cabinet-wiring diagram shall be furnished with each cabinet.

Cabinet Wiring

Cabinet wiring shall conform to the details and diagrams in the Plans.  The Contractor shall trim wiring to eliminate all slack and lace or bind together with nylon wraps or equal.  All terminals shall be labeled.  The cabinet shall be wired completely so that the only requirement to make a field location completely operational is to connect field, power and ground wires to appropriate terminals.

8-20.2(1).GR8

Equipment List And Drawings

8-20.2(1).INST1.GR8

Section 8-20.2(1) is supplemented with the following:

8-20.2(1).OPT1.ITS.DT1

(NWR ITS September 26, 2005)

Approval of Material

When submitting material lists for approval, the Contractor shall identify all revisions or changes to manufacturer names, component names, and model numbers listed in these Special Provisions.  The Contractor shall also include a brief justification for the revision or change.

8-20.3.GR8

Construction Requirements

8-20.3.INST1.ITS.DT1

Section 8-20.3 is supplemented with the following:

8-20.3.OPT1.ITS.docx

(******)

Cabinet Labeling

The Contractor shall mark each ITS device cabinet and transformer cabinet by affixing vinyl lettering which matches the alphanumeric device number as shown in the Plans to the outside of the cabinet. The vinyl letters shall be black on unpainted cabinets and white on painted cabinets. The lettering shall be 4-inch C highway font. The lettering shall be centered horizontally and begin at the top of the cabinet. The first line of text shall be the three number designation of the State Route. The following line(s) shall be the seven character designation of the device(s). The lettering shall be on the side of the cabinet most visible from the roadway. The alphabetical portion of the name shall be lowercase.

The Contractor shall install an engraved nameplate, identifying the power source for each cabinet. The nameplate shall consist of white letters on a red background and be permanently affixed to the inside of the cabinet door. The nameplate text shall read “Cabinet Power Source” in ½ inch nominal letters followed by the service name or transformer name (e.g. SUA173 or 522xf02303), as appropriate, in 1 inch nominal letters.

8-20.3.OPT3.ITS.docx

(******)

Traffic Data Accumulation And Ramp Metering System

Model 334L Cabinet Testing

Traffic data accumulation and ramp metering equipment shall undergo two separate sets of tests prior to final acceptance. The contractor or vendor shall deliver the equipment to the WSDOT Signal Shop in Seattle, Washington for the first test. After installation in the field, WSDOT personnel will performed a second test.

Shop Test

The Contractor or Vendor shall arrange to deliver the equipment for testing to the Northwest Region Signal Maintenance Shop (also known as the Signal Shop or Shop) located at:

3700 9th Ave S

Seattle, WA 98134

Attention: Northwest Region Signals Purchasing

(206) 442 - 2120

Delivery shall be by appointment only. The Contractor or Vendor shall label all equipment and paperwork with the WSDOT Contract number prior to delivery.

The Contracting Agency will limit testing to 25 calendar days for two controller and cabinet assemblies with 2 additional calendar days for each additional controller and cabinet assembly. Shop testing may extend beyond the allowed test period if a cabinet assembly fails any test.

Shop Testing shall consist of a Compliance Test, a Cabinet Functional Test, and a Controller Functional Test.

Compliance Test

Signal Shop personnel will verify that all equipment provided meets the requirements of the plans and all applicable specifications. This includes verification of cabinet documentation, including two cabinet wiring diagrams and a wiring diagram and maintenance manual for all auxiliary equipment furnished in each cabinet. Any documents found to be in error shall be corrected by the Vendor and delivered to the Shop before the cabinet will be released. Equipment such as display panel labels, fiber optic patch panels and communications equipment that is to be installed in the field by the contractor is not required for shop testing.

Cabinet Functional Test

Signal Shop personnel will energize each cabinet and verify that all equipment operates correctly according to all applicable specifications.

Controller Functional Test

Signal Shop personnel shall test all controllers provided for proper operation per all applicable specifications. Controllers may be tested separately or in conjunction with the Cabinet Functional Test.

If a cabinet fails any part of the test, the Engineer will be notified and the cause of the failure shall be corrected by the Contractor or Vendor.

A failed component that can be easily removed without the use of tools (e.g., load switch, loop amp, etc.) shall be replaced by the Contractor or Vendor. After replacement of the faulty component, the cabinet shall be tested again.

Any cabinet that requires troubleshooting or repairs beyond replacement of a pluggable component shall be rejected and removed from the Shop by the Contractor or Vendor for repairs or replacement. The repaired or replaced cabinet shall be returned to the Shop and fully tested per the above requirements.

A failed controller shall be repaired or replaced by the Contractor or Vendor and re-tested by Signal Shop personnel. A failed controller will not delay the release of the cabinet.

The Engineer will notify the Contractor of all rejections. The Contractor or Vendor shall remove all rejected equipment from the Shop within seven calendar days following receipt of the rejection notice.  If not removed accordingly, the Shop will forward the equipment to the Contractor, freight collect.

All equipment except accepted controllers shall be removed from the Shop within seven working days following notice of final approval and acceptance.  If not removed accordingly, the shop will forward the equipment to the Contractor freight collect.  Accepted controllers shall remain in the shop until requested by the Contractor for the turn-on test.

The Contractor will not be granted an extension of time for delays caused by rejected equipment.

Field Test

Field testing will commence following the complete installation of the cabinet and controller, including all field wiring, ramp meter signal displays, flashers, loops, etc., as required by the contract. This testing will consist of Set-up, System Compliance Test, System Functional Test and a Turn-on Test for Ramp Meter installations.

Set-up

Following notification from the Engineer that the data station or ramp meter system is fully installed, ITS Implementation personnel will install the controller and set up the cabinet for operation. This includes connecting the controller to the communications system, assigning and setting the controller’s drop address and tuning loop amplifiers.

System Compliance Test

ITS Implementation personnel will verify that all equipment is installed per the plans and all applicable specifications. This shall include communications gear, fiber-optic patch panels, field wiring, cabinet labels, display panel labels, ramp meter signal display placement, stop line placement, loop placement and alignment, signage and any other equipment required by the contract.

System Functional Test

ITS Implementation personnel will verify that the cabinet and control assembly and all associated field equipment operate correctly according to all applicable specifications. This includes verification of communications with the TMC, verification that all inductive loops are installed and terminated per the plans, verification that all loops detect traffic in the lanes specified in the plans, verification that all flashers operate correctly, verification that all ramp meter signal displays turn on and operate correctly.

Ramp Meter Turn-On

In any cabinet that is to be used as a ramp meter, the Advanced Warning Sign (AWS) flasher and ramp meter signal displays shall be disabled until the ramp meter is ready to be turned on. Ramp metering will not begin until all three field tests above are completed satisfactorily. Any failures or discrepancies shall be corrected by the contractor prior to operating the ramp meter. Within 72 hours before ramp metering is scheduled to begin, ITS Implementation personnel will verify that all cabinet equipment is set up and ready for metering operations. This includes ensuring the AWS flasher and all ramp meter signal displays functioning properly.

8-20.3.OPT4.ITS.docx

(******)

Display Panel Labeling

Existing cabinets as identified in the plans shall have all of the existing loop nameplates removed from the display panel. The display panel shall be cleaned of residue and debris. New nameplates shall be installed according to the new loop layout as per the Field Wiring Chart supplied by the Engineer on request. The new nameplates shall be printed, permanent industrial grade outdoor vynil detector label, 2” x 0.5”, black text on white background.

8-20.3.OPT5.ITS.DT1

Closed Circuit Television System

8-20.3.OPT5.ITS.DT1

Closed Circuit Television System

8-20.3.OPT5(A).ITS.docx

(******)

CCTV Test

The Contractor shall test the CCTV Camera System (camera, pan-and-tilt unit, encoder, and camera control unit) using a Contractor-supplied laptop computer and software.  The laptop computer and software shall remain the property of the Contractor.  All test cables and connections shall be the responsibility of the Contractor.

During each testing phase, the Contractor shall repair, replace, or reconfigure each failed CCTV Camera System at no additional cost to the Contracting Agency.

Bench CCTV Test

The Contractor shall perform a bench test on each CCTV Camera System prior to installation.  The bench test shall be performed at a location proposed by the Contractor and approved by the Engineer.  The bench test shall consist of the following:

1.	Program the CCTV Camera System with IP Settings (IP Address, Subnet Mask, and Gateway) provided by the Engineer.

2.	Display CCTV Camera System video on a Contractor-provided laptop computer and verify that there is a clear image.

3.	Program the camera’s I.D. generator to display the State Route on line 1 and the CCTV camera number on line 2.

4.	Pan and tilt the camera and verify that it moves through its full range.

5.	Zoom and focus the camera in Fast, Medium and Slow modes and verify proper operation in each mode.

6.	In Auto Focus Mode, fully zoom the camera in and out and verify that the camera stays in focus throughout the entire range.

7.	Verify that the CCTV Camera System can be focused in Manual Focus Mode.

8.	Change the iris between Auto and Manual Modes and verify proper operation for each  mode.

9.	Reboot the camera and verify that all settings remain as they were before the reboot.

Field CCTV Test

At each camera control cabinet the Contractor shall connect the camera’s Ethernet cable to a Contractor-provided laptop computer.  The Contractor shall demonstrate to the Engineer the following features of the camera installation:

1.	Verify the CCTV Camera System IP Settings are correct as provided by the Engineer for the CCTV Camera System location under test. Correct the IP Settings as necessary.

2.	Display the CCTV Camera System video on the Contractor-provided laptop computer and verify that there is a clear image.

3.	Program the camera’s I.D. generator to display “WSDOT” followed by the State Route on line 1 and the CCTV camera number on line 2. Verify that the ID is correct for the CCTV Camera System location under test.

4.	Pan and tilt the camera and verify that it moves through its full range.

5.	Zoom and focus the camera in Fast, Medium and Slow modes and verify proper operation in each mode.

6.	In Auto Focus Mode, zoom the camera in and out and verify that the camera stays in focus throughout the entire range.

7.	Verify that the CCTV Camera System can be focused in Manual Focus Mode.

8.	Change the iris between Auto and Manual Modes and verify proper operation in each mode.

9.	Reboot the camera and verify that all settings remain as they were before the reboot.

8-20.3.OPT5(B).ITS.DT1

(NWR ITS October 21, 2003)

HUB CCTV Test

At each hub the Contractor shall connect the camera control device to the EIA-232/422 converter.  The video monitor shall be connected to the BNC port of the camera video receiver for the camera being tested.  In the presence of the Engineer, the Contractor shall demonstrate all of the features listed in the Local CCTV Test section.

8-20.3.OPT5(C).ITS.DT1

(NWR ITS February 11, 2002)

TMC CCTV Test

At the *** $$1$$ *** Traffic Management Center, the Contractor shall witness the TMC CCTV Testing as performed by the Contracting Agency.  The Contracting Agency will attempt to perform all of the Local CCTV Test features through an existing TMS control console at the TMC.

8-20.3.OPT8.ITS.DT1

Variable Message Sign (VMS)

8-20.3.OPT8(A).ITS.docx

(******)

Order of Work

The installation of the sign support structure, sign power service, communications to the WSDOT central computer, delivery from manufacturer, installation, and testing shall be shown in the Contractor’s CPM schedule.  The contractor shall install the VMS within 14 calendar days of delivery from the manufacturer.  Within 24 hours of its installation, power shall be supplied to the VMS and its environmental controls fully operational.  Also, the Contractor shall have the VMS fully operational and ready to begin testing procedures within 14 calendar days of VMS installation.

System Testing

All VMS System components, including but not limited to sign enclosures, control cabinets, controllers and communication and connection components, shall be thoroughly tested for proper operation and compliance with the contract prior to installation and in the field after installation. The testing shall be performed by WSDOT personnel and verified and approved by the Engineer.

Delivery and Assembly

The Contractor or Vendor shall arrange to deliver the equipment for testing to the Northwest Region Signal Maintenance Shop (also known as the Signal Shop or Shop) located at:

3700 9th Ave S

Seattle, WA 98134

Attention: Northwest Region Signals Purchasing

(206) 442 - 2120

Delivery shall be by appointment only. The Contractor or Vendor shall label all equipment and paperwork with the WSDOT Contract number prior to delivery.

The contractor or vendor shall unload and unpack all signs, controller cabinets and other associated equipment at the Signal Shop. All signs shall be placed on level ground or hung on racks by the contractor or vendor as necessary to facilitate testing.

Shop Testing

Following delivery and assembly, WSDOT personnel shall fully test all VMS sign and control components for proper operation and compliance with the contract using approved test procedures. All failures shall be fully repaired by the Contractor or Manufacturer using Manufacturer-approved procedures. Any failed component shall be replaced with a new component having the same part number and specifications as the original failed component. Used parts are not allowed.

All documents must be current and correct.  Should any document require revising or updating, the Contractor shall replace all copies of the erroneous documentation with corrected copies. These documents include but are not limited to:

1.	One Operations and Maintenance Manual for all VMS equipment in each cabinet.

2.	Two wiring diagrams of each cabinet supplied.

3.	Wiring diagrams for all auxiliary equipment furnished.  One set per cabinet.

4.	Auxiliary equipment operations and maintenance manuals.  One set per cabinet.

Any deviation from the testing procedures must be approved by the Engineer. Any deviation from the Plans or Specifications must be repaired by the manufacturer or Contractor, unless approved by the Engineer.

NTCIP Test

VMS signs and controllers will be tested by the Department using the NTCIP Exerciser in place of the Central Computer. The NTCIP Test will be performed for one of each combination of controller model and sign model. The Exerciser shall prove that the DMS sign controller fully complies with the NTCIP requirements of this Special Provision.  The Engineer shall decide any differences in the interpretation of NTCIP Standards.  The Contractor shall be responsible for ensuring that the DMS equipment fully complies with NTCIP standards specified herein. At the Engineer’s discretion, NTCIP testing may be performed at the Signal Shop during Shop Testing or in the field following installation.

Manufacturer Commissioning

Once the equipment has passed Shop Testing and has been installed , the sign will be commissioned by the manufacturer using procedures approved by the Engineer. The commissioning may be done during or after installation, as determined by the Engineer based on operational and scheduling requirements. Commissioning shall be observed by WSDOT personnel. Completed commissioning documentation shall be submitted to the Engineer for approval.

Acceptance Testing

Following the complete installation of the new VMS, a WSDOT representative shall verify proper operation of the sign for the designed application. This test shall verify that the sign is capable of preforming all functions required by the design application and that these functions can be fully controlled remotely from the Dayton Ave. Traffic Management Center.   A representative from the manufacturer shall be present during testing. Acceptance Testing may be performed after or concurrently with Manufacturer Commissioning.

20-day Test

Following Manufacturer Commissioning  and Acceptance Testing, the 20-day Test will commence as scheduled by the Engineer.

A 20-day test period of continuous operation shall be performed.  The test period shall be shown in the contractor's CPM schedule.  The following shall be observed during the test period:

1.	All equipment shall be in working order at the beginning of the test.  Any adjustment or replacement of components shall be considered a malfunction and cause for termination of the test period.

2.	The system shall operate for 20 consecutive days without malfunction.

3.	The VMS shall be communicating with the central computer during the entire 20-day test.  Any loss of communication between the DMS and the central computer shall be considered a malfunction.

4.	Although it is not necessary for the Contractor to provide personnel to be in attendance during the 20-day testing period, upon being informed of a malfunction, the Contractor shall respond within 48 hours with a representative who is thoroughly familiar with the operation of all parts of the system.

5.	Upon detection of a malfunction, the test and test time shall be stopped and the malfunction corrected.  Test time will be reset and a new 20-day test period shall begin.

8-20.3.OPT8(B).ITS.DT1

(NWR ITS February 11, 2002)

VMS Training

The Contractor shall provide 8 hours of VMS system training for 5 Contracting Agency personnel taught by a manufacturer certified instructor.  This shall include classroom instruction at a Contracting Agency facility as well as at the VMS location.  Training shall focus on removal and replacement of sign components and manufacturers standard troubleshooting procedures.

8-20.3.OPT10.ITS.DT1

(NWR ITS April 12. 2004)

Highway Advisory Radio (HAR) System

Sign Assembly

Mounting shall be as shown in the Plans.

Flashing Beacons

The beacons shall be installed as shown in the detail in the Plans.  The flasher units shall be housed within the sign control cabinet.

Sign Lighting Luminaire

The luminaires shall be installed as shown in the Plans.

Sign Control Cabinet

The control cabinet shall be wired and installed as shown in the Plans.

Testing

The Contractor shall demonstrate that upon command from the TSMC the beacons and sign lights can be activated.

8-20.3.OPT11.ITS.DT1

Communication Conduit System

8-20.3.OPT11(A).ITS.docx

(******)

Submittals

Within a minimum of 30 calendar days prior to anticipated construction, the Contractor shall provide all documentation pertaining to the materials and method of execution proposed to satisfy the requirements of this section.  The Engineer's approval is required prior to the committing of any materials or the commencement of any work.

The Contractor shall anticipate a minimum of 30 calendar days for approval or disapproval of each submitted item.  Actual time for the Engineer's review is dependent upon the completeness and appropriateness of the documentation being submitted.  Any deficiencies will require additional time for approval.  Any delays caused by such deficiencies will not be considered grounds for extension of project time.  The Contractor shall anticipate review intervals to ensure project progress in accordance with Section 1-08.3.

The Engineer's approval of any submitted documentation shall in no way relieve the Contractor from compliance with the safety and performance requirements as specified herein.

Submittals required by this item shall include, but not be limited to, the following:

1.	The manufacturer's specifications for cable vaults and pull boxes.

2.	Detailed shop drawings of pull box and cable vault fabrication.

3.	Manufacturer’s specifications for all conduit, fittings and accessories.

4.	Three foot sample of each type (PVC schedule 40 and PVC schedule 80) of conduit with bell ends.

5.	Certificate of compliance with requirements for coefficient of friction and Bellcore GR-356-CORE for innerducts.

8-20.3.OPT11(B).ITS.docx

(******)

Location Wire and Warning Tape

Warning Tape

Warning tape shall be installed in continuous sections for all underground fiber optic conduit installation where trenching is required.  The warning tape shall be installed approximately 6 inches below the surface of pavement or existing grade.  Warning tape shall be installed a minimum of 12 inches into all cable vaults and pull boxes at both ends of the trench.

Location Wire

Wire conductor shall be installed above conduit in continuous sections for all underground fiber optic conduit installation where trenching is required. If conduit is being installed by boring, the location wire shall be installed inside the conduit. A minimum of 6 feet of location wire shall be extended into each cable vault or pull box. The locate wire shall be attached to the “C” channel or the cover hinge bracket with stainless steel bolts and straps.  A 1-foot loop of locate wire shall be provided above the channel as shown in the Plans.  Locator wire shall be placed between the conduits in dual conduit installations or on top of conduits for single conduit installations.

8-20.3.OPT12.ITS.docx

Active Traffic Management (ATM)

(******)

The installation of new ATM signs including lane control sign (LCS), side mount dynamic message sign (SDMS), variable message sign (VMS), and associated equipment shall comply with all construction requirements in the subsection Variable Message Signs special provisions.

Active Traffic Management System Testing

System testing for existing and new ATM signs and controllers shall comply with all testing requirements in the subsection Variable Message Signs special provision.

Testing of the existing ATM sign hardware shall be the responsibility of the Contractor.  These tests shall demonstrate that each component is fully functional and conforms to these Special Provisions.  At a minimum, the tests shall show that all pixels are operational and that the control software provides LED brightness, housing ventilation, and message control. All components that fail a test shall be replaced and re-tested.

The Contractor shall provide the Engineer with a copy of the Field Test reports for each existing ATM sign, once the existing ATM sign equipment is found to be fully functional.  The test reports required by this specification shall include:

1.	A list of all equipment used to perform the tests

2.	A record of each test step, who performed the tests, who witnessed the tests, and the test results

3.	A record of test failures, corrective action taken, and results of the retest

The Engineer reserves the right to perform any independent inspections or tests, which are deemed necessary to ensure that the ATM sign equipment and software complies with the requirements of the Special Provisions.

Acceptance Testing

The System Acceptance Test for existing and new ATM signs shall comply with all requirements of the Acceptance Testing in the subsection Variable Message Signs special provision.

8-20.3.OPT13.ITS.DT1

Communication Cables And Interfaces

8-20.3.OPT13(A).ITS.DT1

(NWR ITS February 11, 2002)

Submittals

Within a minimum of 30 calendar days prior to anticipated construction, the Contractor shall provide all documentation pertaining to the materials and method of execution proposed to satisfy the requirements of this section.  The Engineer's approval is required prior to the committing of any materials or the commencement of any work.

The Engineer will either approve or disapprove each submitted item within 30 calendar days of submittal subject to the completeness of the Contractor's submittal.  Actual elapsed time for the Engineer's review is dependent upon the completeness and appropriateness of the documentation being submitted.  Any deficiencies in the Contractor's submittals shall require additional time for approval.  Any delays caused by such deficiencies shall not be grounds for extension of project consideration dates.  The Contractor shall anticipate review intervals and schedule submittals accordingly to ensure project progress in accordance with Section 1-08.3.

The Engineer's approval of any submitted documentation shall in no way relieve the Contractor from compliance with the safety and performance requirements as specified herein.

Submittals required by this item shall include, but not be limited to, the following:

1.	A material staging plan, should the Contractor propose State owned property as a staging area.

2.	Manufacturer's complete specifications for all communication system cables and, associated electronics and hardware components.

3.	Manufacturer's complete specifications for twisted-pair cable splice enclosures.

4.	A detailed fiber optic and twisted-pair cable installation procedure including the following:

a.	Fiber optic cable cutting lengths reflecting the cable order and reel allocations.

b.	Cable pulling plan which shall state the exact operational procedures to be utilized and which identifies the physical locations for equipment placement, proposed equipment setup at each location, pulling tension on all cables for each pull, staffing, and the pulling methodology for each type of cable.

c.	Exact splice points as provided for herein.

d.	Workforce proposed for all equipment, safety, and manual assist operations

5.	Factory test data sheets for each reel of cable delivered.

8-20.3.OPT13(B).ITS.DT1

(NWR ITS February 11, 2002)

Cable Installation - General

The Contractor shall determine a suitable cable installation method to ensure that all cable installation requirements shall be met in all conduit sections.  All work shall be carried out in accordance and consistent with the highest standards of quality and craftsmanship in the communication industry with regard to the electrical and mechanical integrity of the connections; the finished appearance of the installation; as well as the accuracy and completeness of the documentation.

The Contractor shall make a physical survey of the project site for the purpose of establishing the exact cable routing and cutting lengths prior to the commencement of any fiber optic work or committing any fiber optic materials. Splicing is only allowed for the programmed connection of reels and as shown in the Plans to connect a lateral fiber optic cable to the mainline distribution fiber optic cable.  The Contractor shall submit a cable routing plan that shows the locations of all splices.  All splice locations other than those shown in the Plans must be approved by the Engineer.

All work areas shall be clean and orderly at the completion of work and at times required by the Engineer during the progress of work.

8-20.3.OPT13(C).ITS.docx

(******)

Fiber Optic Cable Installation

Fiber optic cables shall be installed in continuous lengths without intermediate splices throughout the project, except at the location(s) specified in the Plans, or as approved in writing by the Engineer.

The Contractor shall comply with the cable manufacturer's specifications and recommended procedures including, but not limited to the following:

1.	Installation.

2.	Proper attachment to the cable strength elements for pulling during installation.

3.	Bi-directional pulling.

4.	Cable tensile limitations and the tension monitoring procedure.

5.	Cable bending radius limitations.

The Contractor shall protect the loops from tangling or kinking.  At no time during the length of the project shall the cable’s minimum bending radius specification be violated.

To accommodate long, continuous installation lengths, bi-directional pulling of the fiber optic cable shall be permitted.

In all cable vaults, pull boxes, and at all splice locations cable slack of 50 feet shall be left by the Contractor, unless otherwise specified in the Plans.  The 50 feet length of fiber optic cable shall be coiled and secured with tie wraps to racking hardware or as specified in the Plans.

Installation shall involve the placement of fiber optic cables in a specified inner duct as defined in the Plans.  The Contractor shall ensure that inner ducts are secured to prevent movement during the cable installation process.

The pulling eye/sheath termination hardware on the fiber optic cables shall not be pulled over any sheave blocks.

When power equipment is used to install fiber optic cabling, the pulling speed shall not exceed 100 feet per minute.  The pulling tension limitation for fiber optic cables shall not be exceeded under any circumstances.

Large diameter wheels, pulling sheaves, and cable guides shall be used to maintain the appropriate bending radius.  Tension monitoring shall be accomplished using commercial dynamometers or load-cell instruments.

Fiber optic cable lubricant shall be used to reduce pulling tensions for the     installation of each fiber optic cable.

# Patch Cord Installation

# Patch Cords installed within a cabinet shall adhere to the following:

      - Patch cords contained within a patch panel shall not be more than 1 foot longer than required to make the connection.

      - Patch cords between two patch panels shall not be more than 1 foot longer than required to make the connection.

      - Patch cords between a patch panel and a device shall not be more than 2 feet longer than required to make the connection.

      - Patch cords between a patch panel and a device shall be contained inside of ½” or 3/8” split yellow loom.

      - Boots shall be glued to the jacket of the patch cord.

8-20.3.OPT13(D).ITS.DT1

(NWR ITS October 16, 2006)

Fiber Optic Cable Splicing

Field splices shall be located as shown in the plans. No additional splices will be allowed without the approval of the Engineer.

All fusion splicing equipment shall be in good working order, properly calibrated, and meeting all industry standards and safety regulations.  Cable preparation, closure installation and splicing shall be accomplished in accordance with accepted and approved industry standards.

Upon completion of the splicing operation, all waste material shall be deposited in suitable containers for fiber optic disposal, removed from the job site, and disposed of in an environmentally acceptable manner.

The Contractor shall use the fusion method for fiber optic splicing.  Acceptable fusion splicing techniques are:

Local Injections and Detection

Profile Alignment System

The Contractor shall seal all cables where the cable jacket is removed. The cable shall be sealed per the cable manufacturer’s recommendation with an approved blocking material.

The Contractor shall seal all buffer tubes with an approved blocking material to prevent migration of gel into splice trays.

All splices shall be contained in splice trays utilizing strain relief, such as heat shrink wraps, as recommended by the splice tray manufacturer.

8-20.3.OPT13(E).ITS.docx

(******)

Fiber Optic Splice Closure

The mainline and distribution cables shall not occupy the same splice closure. Only cables that are being spliced to each other may occupy a single splice closure. Only one preterminated patch panel stub shall occupy any one splice closure except where more than one preterminated patch panel is needed to terminate a single cable.

Upon sealing the splice closure, the Contractor shall show that the closure maintains 10 psi of pressure for a 1-hour period.

8-20.3.OPT13(F).ITS.docx

(******)

Fiber Optic Cable Labeling

Permanent cable labels shall be used to identify fiber optic cables at each termination point and in every pull box and cable vault. The cable labels shall consist of a self-laminating plastic black and yellow tag with the words “CAUTION FIBER OPTIC CABLE” and with a space for a custom description of the cable being labeled.  The custom portion of the tag shall contain the fiber count, fiber type (SMFO or MMFO), use (mainline, distribution, or other), and cable direction (north, east, south, west).

Patch panels shall be labeled with 3/8”-1/2” printed laminated labels.  The labels shall be located inside the patch panel where they can be read with the door open.  The labels shall provide a description of what fibers are spliced to each port in the panel.  The description shall include port number, fiber purpose, cable direction and fiber numbers (i.e. “Ports 13-24: Distribution South 1-12”).

8-20.3.OPT13(G).ITS.DT1

(NWR ITS June 7, 2004)

Twisted-Pair Copper Cable Installation

The Contractor shall install all OSP cables and associated terminal blocks.

Cables shall be terminated in the communication hubs on a combination connector/protector block, which shall be an AT&T Type 310 bifurcated quick clip terminal block mounted on the wall of the vault.  Protection shall be provided for each pair.  The surge protector shall be solid state, low voltage (60-90 volts) for non-ringing circuits, 130 volts for ringing circuits and shall have a heat coil for sneak current protection, and gold-plated pins.  Protector block ground shall be connected to the ground bus.

Where cables are terminated at terminal blocks in cabinets, the same pair assignment shall be maintained.

8-20.3.OPT13(H).ITS.DT1

(NWR ITS February 11, 2002)

Cable Racking in Pull Boxes and Cable Vaults

The Contractor shall rack the cable in vertical figure eight loops, which shall permit pulling slack from the vaults without introducing twist to the cable.

Cables shall be secured in racked positions with nylon ties.  Identification or warning tags shall be securely attached to the cables in at least two locations in each pull box or cable vault.

All coiled cable shall be protected to prevent damage to the cable and fibers.  Racking shall include securing cables to brackets (racking hardware) that extend from the side walls of the pull box.

All racking hardware shall be stainless steel.

8-20.3.OPT13(I).ITS.DT1

(NWR ITS October 16, 2006)

As-Built Records

The Contractor shall provide the Engineer with a cable route diagram for all installed fiber optic and twisted pair cables.  The diagram shall show the actual cable routes and "meter marks" where each cable enters and exits pull boxes, cable vaults, junction boxes, splices and termination points.  The Contractor shall record these points during cable installation.  The diagram shall also include all ITS device locations as well as the location and quantity of slack cable.  The cable route diagram shall be submitted to the Engineer as part of the Fiber Cable Testing documentation.

8-20.3.OPT13(J).ITS.DT1

(NWR ITS May 5, 2014)

Fiber Optic Cable Testing

The installed optical fiber cable shall be tested for compliance with the transmission requirements of this specification, the cable and hardware manufacturer's specifications, and prescribed industry standards and practices.

Prior to commencing acceptance testing, the Contractor shall complete the installation of the fiber optic system.  This includes sealing the splice closures, completing the splicing and racking the cables in the pull boxes and cable vaults.

All testing values shall be in metric.

Types of Testing

The two required acceptance tests for optical fiber cable system certification are:

Power Meter testing

Optical Time Domain Reflectometer (OTDR) testing

Power Meter Testing

Power meter testing shall be used to measure the end-to-end attenuation of each new fiber installed between a field device and a communications hub as well as between communications hubs.  Power meter testing shall be performed at the 1310 and 1550 nanometer wavelength in both directions.

Prior to commencing testing, the Contractor shall submit the manufacturer and model number of the test equipment along with certification that the power meter has been calibrated within 12 months of the proposed test dates.

The following information shall be documented for each fiber test measurement:

1.	Fiber/Strand #

2.	Fiber type (Singlemode or Multimode)

3.	Cable, tube, and fiber IDs

4.	Near end and far end test locations

Use device names in Contract plans

5.	End-to-end attenuation

In each direction and the bidirectional average

6.	Length of span being tested

7.	Date, time, and operator

8.	Wavelength

Optical Time Domain Reflectometer (OTDR) Testing

An optical time domain reflectometer (OTDR) with recording capability shall be utilized to test the end-to-end transmission quality of each optical fiber.  Quality tests shall consider attenuation, reflectance, and discontinuities.  The OTDR shall be equipped with 1310 nanometer and 1550 nanometer light sources for singlemode optical fibers.  The OTDR shall be capable of providing electronic and hard copy records of each test measurement.

The Contractor shall utilize a dead-zone box (a.k.a. launch reel) containing 1 km of optical fiber, when performing OTDR tests.  The dead-zone box shall be located between the OTDR and the fiber optic connector of each strand tested.

Each new fiber shall be tested in both directions at the 1310 and 1550 nanometer wavelengths. Existing fibers that are spliced to or re-spliced as part of this contract shall also be tested in both directions and at both wavelengths.

The following information shall be documented for each fiber test measurement:

1.	Fiber/Strand #

2.	Fiber type (Singlemode or Multimode)

3.	Cable and fiber IDs

4.	X-Y plot scaled for fiber length

- The X-axis (Distance) shall be scaled such that the beginning of the trace starts with the OTDR/dead-zone interface.  The end of the trace shall extend no more than 1 km beyond the end of the test span.

- The Y-axis (dB) shall be set to maximize the trace.  The bottom of the Y scale shall begin above the noise floor and the top of the scale shall be no more than 5 dB higher than the largest event.  No events or reflections shall be cut off.

5.	Near end and far end test locations

Use device names in Contract plans

6.	Date, time, and operator

7.	Wavelength

8.	OTDR Settings

- Index of Refraction

- Averaging time (Minimum of 30 seconds)

- Pulse Width (to provide a smooth trace, excluding events)

9.	Table of Events that includes:  Event ID, Type, Location, Loss, and Reflection.

- Events are defined as:

1.	Any reflectance event in excess of -60 dB

2.	Any loss occurrence in excess of 0.05 dB

3.	Any splice location regardless of loss

4.	Beginning and end of span

The beginning of the span shall be denoted by the “A-Marker”.  This marker shall be placed just to the left of the spike of the dead-zone box / fiber interface.

- The end of the span shall be denoted by the “B-marker”.  This marker shall be placed just to the left of the end-of span reflection spike.

Fiber Optic Performance Requirements

1.	Splice Loss:

Shall not exceed 0.20 dB in one direction

Bidirectional Average shall not exceed 0.15 dB

2.	Reflectance:

Shall not exceed -55 dB

Fiber Cable Testing Documentation

The Contractor shall submit one hard copy and one electronic copy of the fiber test results to the Engineer for approval. Only one OTDR test result shall be on each page.  The Contractor shall take corrective actions on portions of the fiber installation determined to be out of compliance with these specifications.

Upon acceptance of the cable installation and test results, the Contractor shall submit three hard copies and three electronic copies of the fiber test results to the Engineer.

Hard copy submittals shall be bound in 3-ring binders.  Each 3-ring binder shall have the following information on the front and side:

1.	The title “Fiber Optic Test Results”

2.	The name of the roadway(s) where fiber was installed

3.	Contract name and number

4.	Date

The front cover shall also include the following:

1.	The size of each cable installed and the beginning and ending mileposts of each cable replaced.

2.	The company name address and phone number that did the fiber optic work

Each 3-ring binder shall also include a table of contents and index dividers for each cable segment and each direction tested.  The electronic submittals shall be on compact discs and include one licensed copy of the applicable OTDR reader program.

The following information shall be included in each test result submittal:

1.	Contract number, contract name, contractor name and address

2.	Dates of cable manufacture, installation, and testing

3.	Cable specifications

Manufacturer data sheet

Helix Factor

Date of manufacture

4.	Fiber (Glass) specifications

Manufacturer and Part #

Index of Refraction

Optical performance (loss/km)

Mode Field Diameter

5.	As-Built Records (In accordance with the Special Provisions)

6.	OTDR test results – No more than one test per page

7.	Power Meter test results

Within 30 days of submitting the test results, the Contractor, in the presence of the Engineer, shall re-test a minimum of 5% of the previously tested locations to validate the test results.  A 5% sample will be selected randomly from the terminal device locations.

8-20.3.OPT13(K).ITS.DT1

(NWR ITS September 9, 2002)

Twisted-Pair (TWP) Copper Cable Testing

The Contractor shall perform a Field Acceptance Test on the installed cable.  Each pair shall be tested for frequency attenuation between the communication hub and each ITS device.  The State will provide a witness during the tests and the test results shall be documented as prescribed elsewhere in this specification.

Any pairs showing attenuation greater than 2 dB per mile at 1 kHz shall be cause for rejection of the cable.  The Contractor shall replace any cable failing this test at no additional expense to the Contracting Agency.  The Contractor shall provide all test equipment necessary to perform the tests.

All pairs of each underground cable shall be tested for continuity, polarity, shorts, grounds, longitudinal balance, and both resistive and impedance losses consistent with the manufacturer's specifications and standard telecommunication industry requirements

Each TWP copper cable intended primarily for data communication applications shall be tested end-to-end from the controlled environment vault cable termination point to the interface at the traffic control device.  The transmission test procedure shall include the continuity testing of each pair within each TWP cable from the outlet in the termination panel in the vault to the termination outlet at each device location.

The Contractor shall ensure that all individual wires in all TWP cables have been terminated consistent with the wire insulation color to termination pin requirements set forth in this Special Provision.

The Contractor shall document the transmission quality test results for 50% of the pairs in each cable of the installed TWP cable and provide documentation for each cable that the cable meets or exceeds the manufacturer's published specifications and otherwise complies with the requirements set forth in this specification for characteristic impedance, longitudinal balance, resistive and impedance losses, and near-end crosstalk.

The Contractor shall provide the Engineer with the manufacturer and model number of the test equipment and the equipment calibration procedures to be used prior to conducting all tests.

The Contractor shall test each underground cable end-to-end from the controlled-environment vault-termination block to the terminal block at each cable pedestal or other outside plant terminal equipment.  The Contractor shall provide actual test readings for each of the following items to verify the required transmission criteria:

DC Resistance - The resistance of any conductor in any cable shall not exceed 20 ohms per 1000 feet.

DC Resistance Unbalance - The resistance unbalance between the two conductors of any pair shall not exceed 5%.

Ambient Noise Measurements - The Contractor shall measure the ambient noise level in dBm0 to determine the level of noise on each cable being tested.  The distant end of the pair being tested should be terminated with a 600-ohm resistor.  At the near end, an HP-3551 or equivalent transmission measuring set should be configured for conducting a noise reading test.  Cable pairs being sampled shall provide an ambient noise figure of 30 Dbm0 (-60 dBm) or better.  The Contractor shall record all readings.

Shield Continuity -Test and measurements shall be made to assure that all underground cable shields are continuous from end-to-end.  Each shield shall show a resistance of not more than .75 ohms per 1000 feet.

Within 30 days of submitting the test results, the Contractor, in the presence of the Engineer, shall re-test a minimum of 5% of the previously tested locations to validate the test results.  A 5% sample will be selected randomly from the terminal device locations.

8-20.3.OPT13(L).ITS.docx

(******)

Ethernet Switches IP Addresses

The Contractor shall submit a list of all Ethernet devices and the associated cabinet identification numbers through the Engineer to the ITS Engineer.  The Contractor shall program all supplied information into the devices including, time server, gateway, mask, and address, system name, and location.   The Contractor shall allow 10 working days to receive the Ethernet IP information from the Engineer.

8-20.3.OPT24.ITS.docx

(******)

Video, Voice, & Data Distribution And Transmission Systems

The Contractor shall provide the following:

At Dayton Avenue new TMC

Description:							Quantity

Ethernet Switch with Device Server (RS910)		      1

Documentation

Documentation for each system element shall consist of the manufacturer's name and model number, serial number when available, materials and operating specifications, wiring schematic and parts list, owners manuals, factory service manuals, and procedures for factory testing and system acceptance testing specified elsewhere herein.  The Contractor shall submit three copies of the documentation specified above prior to the installation of the cable or components described in the submittal.  In addition, the Contractor shall submit three copies of an overall system wiring schematic and termination chart for the installed TMS elements (operation and maintenance manuals).  All documentation for each individual element shall be neatly bound in such a way that the information is secured together and is totally legible without removing the information from the binding.  This documentation shall be in addition to any other data, shop drawings, etc. required to be submitted as specified in these Special Provisions.

8-20.3.OPT25.ITS.DT1

(NWR ITS February 23, 2009)

Communication Hub / Concrete Universal Enclosure (CUE)

The Contractor shall provide shop drawings of the CUE's electrical system, construction, and all component locations and connections.  The Contractor shall also provide all cabling for interfacing the CUE alarm contacts with the SONET equipment.

Site Preparation

Care shall be exercised in site preparation, in positioning the enclosure on the selected site, and in finish grading to avoid the possibility of a flood condition that would submerge the entranceway.  The enclosure shall be placed on a 6-inch sand drainage blanket.  The structure excavation Class B, shoring or extra excavation, sand drainage blanket, backfill and compaction shall be in accordance with Section 2-09.

Installation

The CUE shall be shipped in one piece to the installation site and installed into the excavation without the need for personnel to be in the excavation.  Multiple-piece enclosures requiring assembly will not be accepted.   Additionally, the one-piece enclosure shall be structurally and physically suitable for the installation of the system equipment prior to final shipment to the job site.

A separate, internal ground point shall be provided for the enclosure electrical system and the Contracting Agency's system equipment and shall be labeled as "System Ground."  Earth grounding for this point shall be accomplished with two external 5/8-inch by 8-foot copper ground rods and ground wires provided by the enclosure installer.

Enclosure Electrical System

The enclosure shall be equipped for 120/240 volt, single-phase, 60 Hz, 100 AMP underground utility service from a remote meter pedestal.  All conduits shall enter the power transfer switch enclosure via 2.5-inch diameter NPT threaded couplings.  A dielectric connection shall be provided at the vault to insure that no grounding is provided by the conduits.  The electrical service conductors shall include ground conductor(s).

The distribution system shall be rated 100 AMP for both Utility and Auxiliary sources.  The Utility Service shall connect to a 100 AMP Main Breaker which shall be an integral component of a Power Transfer Switch (PTS).  In the NORMAL Position, the Power Transfer Switch	 (PTS) shall connect the Utility Service through to a 125 AMP Distribution Panel (DP) that contains all Branch Circuit (Breaker) Protection.

8-20.3(1).GR8

General

8-20.3(1).OPT1.ITS.DT1

(NWR ITS October 10, 2005)

Existing System Disruption and Restoration

The Contractor shall use every precaution to ensure that no contract work causes disruptions to the existing systems, except those disruptions that are planned and approved in advance, as defined herein.

Existing systems include, but are not limited to, the following:

A.	All ITS field devices, such as ramp meter, data collection, and CCTV systems, within the project construction limits.

B.	Fiber optic and TWP data and video communication systems on *** $$1$$ ***.

Planned Disruptions

Contract work may require disruptions to existing systems, circuits, and equipment.  The Contractor shall schedule the work and predetermine the affected system(s), extent, start time, and duration of planned disruptions.  Planned disruptions shall be scheduled between the hours of 8 P.M. and 4 A.M. If traffic control is required for this work, the Contractor shall also adhere to the allowable closure hours listed in the Special Provisions. Failure of the Contractor to restore disrupted systems and equipment prior to 4 A.M will constitute an unplanned disruption, and the "Restoration Procedure" below will apply.

Requirements

Twenty-one calendar days prior to planned disruptions of any existing system, circuit, or equipment, the Contractor shall submit to the Engineer for approval a written Disruption Request.  Each Disruption Request shall include the system(s) to be affected, the disruption start date and time, and the estimated duration required.  The Contractor shall submit a separate, numbered Disruption Request for each planned disruption.  Disruption Request approval or rejection will be returned to the Contractor in writing by the Engineer at least seven calendar days prior to the proposed start of the disruption.  The Engineer may reject a requested time or duration and verbally recommend an alternate time or duration agreeable to both the Contractor and the Contracting Agency.

Restoration Procedure

Any unplanned disruptions determined by the Engineer to be caused by the actions of the Contractor or the Contractor's representative(s) shall be corrected by the Contractor at no additional cost to the Contracting Agency.

Upon the occurrence of an unplanned disruption and subsequent notification by the Engineer, the Contractor shall immediately stop all other ITS work in progress, in accordance with Section 1-08.6, and shall expend all efforts to restore the disrupted system(s) or correct the problem causing the disruption.  The Contractor will not be granted an extension of time for delays caused by the repair of disrupted systems. Unplanned disruptions shall result in the assessment of liquidated damages in accordance with the subsection Liquidated Damages of the Special Provision PROSECUTION AND PROGRESS.

8-20.3(1).OPT2.ITS.DT1.docx

(******)

ITS System Order of Work

The Contractor shall submit for review and approval a proposal for accomplishing the ITS work to the Engineer along with a copy to:

ITS Engineer

15700 Dayton Avenue North

P.O. Box 330310 MS82-120

Seattle, WA  98133-9710

(206) 410-0020

The proposal shall be approved before any ITS fieldwork begins.  The proposal shall include a critical path for ITS construction which shows dates of disconnection, reconnection, and installation of the following ITS components as applicable to this contract:

1.	Traffic Data Accumulation And Ramp Metering System

2.	Communication Conduit System

3.	Communication Cable and Interfaces

4.	Video, Voice & Data Distribution and Transmission System

The critical path shall also indicate all roadway lane shifts or closures that will be in effect during ITS construction.

8-20.3(1).OPT3.ITS.docx

(******)

Removal and Delivery of Existing ITS Equipment

Where identified in the Plans, the Contractor shall remove and deliver the existing devices to:

3700 9th Ave. S.

Seattle WA 98134

Attention: Signal Stores Supervisor

(206) 442-2121

FAX: (206) 442-2147

Five days written advance notice shall be given to both the Engineer and the electrical parts specialist at the address listed above.  Delivery shall occur between the hours of 8:00 a.m. and 1:00 p.m. Monday through Friday by appointment with Northwest Region Signals Purchasing only.  Material will not be accepted without the required advance notice.

Equipment damaged during removal or delivery shall be repaired or replaced to the Engineer’s satisfaction at no cost to the Contracting Agency.

8-20.3(5).GR8

Conduit

8-20.3(5)A1.ESP.DT1

Fiber Optic Conduit

8-20.3(5)A1.INST1.ESP.DT1

Section 8-20.3(5)A1 is supplemented with the following:

8-20.3(5)A1.OPT1.ESP.DT1

(NWR June 24, 2013)

When multiple conduits are installed in the same trench, one location wire shall be placed between conduits.  When multiple conduits are installed in the same boring, one locate wire is required for the conduit bundle.

Location wire routed into pull boxes or cable vaults shall be attached to the “C” channel or the cover hinge bracket with stainless steel bolts and straps.  A 1-foot loop of locate wire shall be provided above the channel as shown in the Plans.

8-20.3(5)A2.ESP.DT1

ITS and Cabinet Outer and Inner Duct Conduit

Section 8-20.3(5)A2 is supplemented with the following:

8-20.3(5)A2.INST1.ESP.DT1

Section 8-20.3(5)A2 is supplemented with the following:

8-20.3(5)A2.OPT1.ESP.DT1

(NWR June 24, 2013)

Conduit Seal

Existing conduits, entering cabinets, that are scheduled to have cables added or removed shall be sealed with an approved mechanical plug or waterproof foam at both ends of the conduit run.

Existing Outer duct and inner duct conduit, entering cabinets, that are scheduled to have cables added or removed shall be sealed according to this section.

8-20.3(5).OPT1.ITS.docx

(******)

Cabinet Conduit Sealing

All conduits entering pad mounted cabinets and all conduits entering ITS hubs shall be sealed with an approved mechanical plug at both ends of the conduit run.  Conduit duct seal will not be accepted.  This applies to all new conduits and all existing conduits that cables have been added to or removed from.

Pad mounted cabinets shall include all cabinets installed on a concrete foundation.

8-20.3(6).GR8

Junction Boxes, Cable Vaults, and Pull boxes

8-20.3(6).INST1.ESP.DT1

Section 8-20.3(6) is supplemented with the following:

8-20.3(6).OPT1.ESP.docx

(******)

Junction Boxes, Cable Vaults, and Pull Boxes

Unless otherwise noted in the Plans or approved by the Engineer, junction boxes, cable vaults and pull boxes shall not be placed within the traveled way or paved shoulders.

The lid of any cable vault or pull box connected directly to a cabinet foundation shall be at a lower elevation than the cabinet foundation.

A screened, 2-inch drain pipe shall be provided between all cable vaults or pull boxes and any slope, drainage ditch, swale or pond within 100 feet.

Junction boxes, pull boxes and cable vaults shall not be installed within the clear working space in front of the doors of any cabinet.  The clear working space is defined as the width of the cabinet doors and 36 inches deep.

Install a concrete collar around each new Type 1 and Type 2 junction box installed in soil. Install a concrete collar around each existing Type 1 and Type 2 locking lid junction box, installed in soil, and scheduled to be relocated or adjusted.

The concrete collar shall be one foot wide and one foot deep, rectangular in shape, and installed around the entire perimeter of the junction box.  The exposed portions of the collar shall be formed to have a neat appearance. The top outer edges of the collar shall have a 3/4 inch chamfer.  The concrete mix design shall be commercial concrete per standard specification 6-02.3(2)B.

All junction boxes, cable vaults, and pull boxes placed within the traveled way or paved shoulders shall be heavy-duty.

Wiring shall not be pulled into any conduit until all associated junction boxes have been adjusted to, or installed in, their final grade and location, unless installation is necessary to maintain system operation. If wire is installed for this reason, sufficient slack shall be left to allow for future adjustment.

When junction boxes, cable vaults and pull boxes are installed or adjusted prior to construction of finished grade, pre-molded joint filler for expansion joints may be placed around the junction boxes, cable vaults and pull boxes. The joint filler shall be removed prior to adjustment to finished grade.

Adjustments involving raising or lowering of new or existing junction boxes shall require conduit modification if the resultant clearance between top of conduit and the junction box lid becomes less than six inches or more than ten inches. Wiring shall be replaced if sufficient slack is not maintained.

The six-inch gravel pad required in Standard Plan J-40.10.01 and J-40.30.00 shall be maintained. When existing junction boxes do not have this gravel pad, it shall be installed as part of the adjustment to finished grade.

Where conduit and junction boxes are placed in barrier, the prime Contractor shall coordinate the work of the Contractor constructing the barrier and the electrical Contractor so that each junction box placed in the barrier is placed in correct alignment with respect to the barrier, with the face of the box flush. The junction box shall be parallel to the top of the barrier within a 1-degree tolerance. If any point on the face of a junction box placed in barrier is recessed more than 1/8 inch from the surface of the barrier, the Contractor shall install a box extension per the Engineer’s approval and grout around the extension or remove and replace the entire section of barrier.

Heavy-duty Type 4, 5 and 6 junction boxes, cable vaults and pull boxes shall be installed in accordance with the following:

1.	Excavation and backfill shall be in accordance with Section 2-09. Excavation for junction boxes, cable vaults and pull boxes shall be sufficient to leave one foot in the clear between their outer surface and the earth bank.

2.	Junction boxes, cable vaults and pull boxes shall be installed on a level 6-inch layer of crushed surfacing top course, in accordance with 9-03.9(3), placed on a compacted or undisturbed foundation. The crushed surfacing shall be compacted in accordance with Section 2-09.3(1)E.

3.	After installation, the lid/cover shall be kept bolted down during periods when work is not actively in progress at the junction box, cable vault or pull box.

4.	Before closing the lid/cover, the lid/cover and the frame/ring shall be thoroughly brushed and cleaned of all debris. There shall be absolutely no visible dirt, sand or other foreign matter between the bearing surfaces.

5.	When the lid/cover is closed for the final time, a liberal coating of anti-seize compound shall be applied to the bolts and nuts and the lid shall be securely tightened.

6.	Hinges on the Type 4, 5 and 6 junction boxes shall be located on the side of the box, which is nearest to adjacent shoulder. Hinges shall allow the lid to open 180 degrees.

8-20.3(8).GR8

Wiring

8-20.3(8).INST1.ITS.DT1

Section 8-20.3(8) is supplemented with the following:

8-20.3(8).OPT1.ITS.DT1

(NWR ITS February 23, 2009)

Traffic Data Accumulation And Ramp Metering System

Existing cabinets with new loops installed shall have all of the existing loop nameplates removed from the display panel.  The display panel shall be cleaned of residue and debris.  New nameplates shall be installed according to the new loop layout.  The new nameplates shall be in accordance with the contract details and specifications.

8-20.3(9).GR8

Bonding, Grounding

8-20.3(9).INST1.ITS.DT1

Section 8-20.3(9) is supplemented with the following:

8-20.3(9).OPT1.ITS.DT1

(NWR ITS February 23, 2009)

Where existing ITS conduits are utilized, an equipment-grounding conductor shall be installed except for conduits with innerduct.

In addition to the conductors called for in the contract, all ITS conduits without innerduct shall be installed with an equipment-grounding conductor and bonding jumpers sized per NEC 250-122 , with the exception that the minimum size shall be 8 AWG.

All new and existing junction boxes, cable vaults and pull boxes that an equipment-grounding conductor is pulled to shall be bonded in accordance with Section 8-20.3(9).

Location wires shall not be connected to the equipment-grounding system.  See “Location Wire and Warning Tape” sections in subsection Communication Conduit System for attachment of location wires.

Supplemental grounding shall be provided at signal standards for ramp meters and steel sign posts for advance warning signs.  Foundations for these standards shall be installed with a bare 4 AWG copper wire, which is connected to the reinforcing cage with an approved acorn clamp or exothermic weld and routed to connect to the pole at the grounding lug.

8-20.3(14)C.GR8

Induction Loop Vehicle Detectors

8-20.3(14)C.OPT4.ESP.DT1

(NWR February 22, 2005)

In Section 8-20.3(14)C, Items 2 and 11 and the last two sentences of Item 4 are deleted.

8-20.3(14)C.INST1.ESP.DT1

Section 8-20.3(14)C is supplemented with the following:

8-20.3(14)C.OPT1.ESP.DT1

(NWR August 16, 2010)

# Round Loops

Round loops shall be constructed in accordance with the following requirements:

1.	Loop conductor and lead in cable shall conform to these Special Provisions.

2.	Round sawcuts shall be six feet in diameter and shall be constructed using equipment designed for cutting round loops. The equipment shall use a concave, diamond-segmented blade. The sawcuts shall be normal to the pavement surface and shall be a minimum of 0.25 inches wide. The sawcut depth shall be a minimum of 2 5/8 inches and a maximum of three inches measured at any point along the perimeter, except on bridge decks. Other methods of constructing the round sawcut, such as anchoring a router or flat blade saw, will not be allowed.

3.	The bottom of the sawcut shall be smooth. No edges created by differences in sawcut depths will be allowed.

4.	All sawcut corners shall be rounded to a minimum 1.5 inch radius.

5.	All sawcuts shall be cleaned with a 1000 psi high pressure washer as certified by the manufacturer's label on the machine or as measured by an in line pressure gauge. Wash water and slurry shall be vacuumed out and the sawcut shall be blown dry with compressed air. Disposal of the wash water and slurry shall comply with the requirements of Section 1-07.5(3) and the Special Provision LEGAL RELATIONS AND RESPONSIBILITIES TO THE PUBLIC.

6.	Loops shall be installed after grinding and prior to the final lift of roadway surfacing material.

7.	The conductor shall be installed one turn on top of the previous turn.  All turns shall be installed in a clockwise direction. The conductors shall be secured to prevent floating with 2-inch lengths of high temperature foam backer rod sized for a snug fit. The backer rod shall be spaced at 2-foot intervals around the perimeter of the sawcut and at corners.

8.	Installation of the sealant shall completely encapsulate the loop conductors. A minimum of one inch of sealant shall be provided between the top of the conductors and the top of the sawcut. The top of the sealant shall be flush to 1/8 inch below the top of the sawcut.

9.	Use of kerosene solvent is prohibited.

8-20.3(14)C.OPT2.ESP.DT1

(NWR February 11, 2013)

Loop Sealant

Loop sealants shall be installed per manufacturer’s recommendations.

If 3M Black 5000 sealant is used, it shall be installed so that the sealant is protected from wheel tracking prior to the sealant being fully cured.  When 3M Black 5000 loop sealant is installed below the final lift of an HMA installation, a minimum of 5 consecutive days of cure time is required before the final lift is installed.

8-20.3(14)C.OPT3.ESP.docx

(******)

Existing Traffic Loops

The Contractor shall notify the Area Traffic Engineer through the Engineer a minimum of five working days in advance of pavement removal or grinding in areas with existing loops.

After grinding, the Contractor shall perform the field tests specified in Section 8-20.3(14)D on loops identified on the plans.  The test results shall be recorded and submitted to the Engineer.  Loops that fail any of these tests shall be replaced within three calendar days of the failure.

Loops that fail the tests, as described above, and are replaced shall be installed in accordance with current WSDOT design standards and Standard Plans, as determined by the Engineer.

If after grinding it is determined that loop backer rods are exposed or damaged, and the loop has passed the field tests specified in Section 8-20.3(1)D, the backer rod shall be replaced and the loop resealed with sealant in accordance with these special provisions.

8-20.3(14)C.OPT3.ITS.DT1

(NWR ITS February 23, 2009)

Traffic Data Accumulation And Ramp Metering System

ITS Traffic Data and Speed Induction Loop Detectors - Spacing

Traffic data and speed loops shall be installed 17 feet (± 1 inch) apart, measured from leading edge to leading edge in each lane, as detailed in the ITS plans.  Loop spacing not meeting this requirement shall be reinstalled, by the Contractor, in accordance with these provisions at no additional charge to the Contracting Agency.

With the approval of the Engineer, the loop lead in junction box and the entire loop array (set) may be shifted up to 100 ft maximum, where the plan loop locations call for the loops to be installed in existing pavement with joints or severe cracking.  If required, additional conduit and junction boxes necessary for loop shifting shall be addressed in accordance with Section 1-04.4.

8-20.3(14)D.GR8

Test for Induction Loops and Lead-in Cable

8-20.3(14)D.INST1.ESP.DT1

Section 8-20.3(14)D is supplemented with the following:

8-20.3(14)D.OPT1.ESP.DT1

(NWR October 5, 2009)

Induction Loop Tests

Test A and Test D are revised as follows:

Test A – The DC resistance between the 2 lead-in cable wires, including the loop, shall be measured by a volt ohmmeter.  The resistance shall not exceed 5-ohms or lower the Q of the circuit below 5 where Q is equal to the “Inductive Impedance @ 50 kHz” divided by “Resistance”.

Test D - An inductance test shall be made to determine the inductance level of each inductance loop.  The Contractor shall record the inductance level of each inductance loop installed on the project and shall furnish the findings to the Engineer.  An induction level, as measured from the controller cabinet, below 50-microhenries is considered a failure.

8-20.3(14)D.OPT3.ESP.docx

(******)

Existing Lead-in Cable Test

When new induction loops are scheduled to be installed and spliced to an existing two-conductor shielded detector lead-in cable, the Contractor shall perform the following:

1.	Disconnect the existing detector lead-in cable in the controller cabinet and at the loop splice.

2.	Megger test both detector lead-in cable conductors.  A resistance reading of less than 100-megohms is considered a failure.

3.	Detector lead-in cables that fail the test shall be replaced and then retested.

4.	After final testing of the detector lead-in cable, the loop installation shall be completed and the loop system tested according to Tests A, C and D as revised by these Special Provisions.

5.	Connect the detector lead-in cables in the controller cabinet.

8-20.3(14)D.OPT4.ESP.docx

(******)

Existing Loop Test

When two-conductor shielded detector lead-in cable is scheduled to be installed and spliced to an existing loop, the Contractor shall perform the following:

1.	Disconnect the existing loop from the detector lead-in splice.

2.	Megger test the existing loop wire.  A resistance reading of less than 100-megohms is considered a failure.

3.	Loops that fail the test shall be replaced and then retested.

4.	After the final testing of the loops, the detector lead-in cable installation shall be completed and the loop system tested according to Tests A, C and D as revised by these Special Provisions.

8-20.4.GR8

Measurement

8-20.4.INST2.ESP.DT1

Section 8-20.4 is supplemented with the following:

8-20.4.OPT1.ESP.docx

(******)

No specific unit of measurement will apply to the lump sum items for Traffic Data Accumulation And Ramp Metering System, Communication Conduit System,  Communication Cables and Interfaces or Video, Voice & Data Distribution And Transmission Systems. However, measurement will be for the sum of all items for a complete system to be furnished and installed.

8-20.5.GR8

Payment

8-20.5.INST1.GR8

Section 8-20.5 is supplemented with the following:

8-20.5.OPT1.ITS.DT1

(NWR ITS October 4, 2004)

“Closed Circuit Television System”, lump sum.

“Communication Conduit System”, lump sum.

“Communication Cables and Interfaces”, lump sum.

“Video, Voice & Data Distribution & Transmission System”, lump sum.

“Highway Advisory Radio System”, lump sum.

“Variable Message Sign”, lump sum.

“Environmental Sensor Station”, lump sum.

“Permanent Traffic Recorder Station”, lump sum.

The lump sum contract price for “Closed Circuit Television System”, “Communication Conduit System”, “Communication Cables and Interfaces”, “Video, Voice & Data Distribution & Transmission System”, “Highway Advisory Radio System”, “Variable Message Sign”, “Environmental Sensor Station”, and “Permanent Traffic Recorder Station”, shall be full pay for the construction of the complete Intelligent Transportation System, modifying existing systems, or both, as shown in the Plans and herein specified including excavation, backfilling, concrete foundations, conduit, wiring, restoring facilities destroyed or damaged during construction, salvaging existing materials, and for making all required tests. All additional materials and labor, not shown in the Plans or called for herein and which are required to complete the Intelligent Transportation System, shall be included in the lump sum contract price.