KOBRA 385 C2 EVRAK İMHA MAKİNESİ                 TEKNİK ŞARTNAMESİ

- MAKİNELERİN KAĞIT KESME BIÇAKLARI ÖZEL SERTLEŞTİRİLMİŞ ÇELİKTEN OLMALI; ATAŞ TEL ZIMBA TOPLU İĞNELERE DAYANIKLI OLMALIDIR.

- MAKİNELERE YANLIŞ VERİLEN EVRAKLAR, GERİ ALMA TUŞU İLE GERİ ALINABİLMELİDİR.

- MAKİNE, KAĞIDI GÖRDÜĞÜNDE OTOMOTİK ÇALIŞABİLMESİ İÇİN, ELEKTRONİK SENSOR DİZAYNINA VE ELEKTRİK TASARRUFU SAĞLAYAN BİR  SİSTEME  SAHİP OLMALIDIR.

- MAKİNELERİN GÖVDE VE DEPOLARI METAL, MOTOR KAPORTA KISMI  SERT PLASTİKTEN  ESTETİK, SESİ AZALTIR ÖZELLİĞE SAHİP OLMALIDIR.

- MAKİNELERİN  VOLTAJI 230 VOLT, GÜCÜ İSE 460 WATT  OLMALIDIR.

- KAĞIT KESİM ÖLÇÜSÜ EN AZ 1,9 x 15 MM VE ÇAPRAZ KESİM  OLMALIDIR.

- MAKİNA AYNI ANDA EN AZ 9/11 ADET  (A4 70gr/ m²) KAĞIT İMHA EDEBİLMELİDİR.

- GÜRÜLTÜ DERECESİ  MAXİMUM 61 dba OLMALIDIR

- DEPO KAPASİTESİ  130  LT OLMALIDIR.

- MAKİNELERİN KAĞIT BESLEME AĞIZ GENİŞLİĞİ  EN AZ 385 MM OLMALIDIR

- GİZLİLİK DERECESİ DIN 32757 STANDARDINDA EN AZ  4 OLMALIDIR.

- MAKİNENİN KAPAĞI AÇILDIĞINDA MAKİNE OTOMATİK OLARAK STOP ETMELİDİR.

- MAKİNENİN DEPOSU DOLDUĞUNDA OTOMATİK OLARAK IŞIK GÖSTERGESİ İLE İKAZ ETMELİ VE MAKİNE STOP ETMELİDİR.

- MOTOR HIZI 0,1 OLMALIDIR VE 24 SAAT ÇALIŞABİLME KAPASİTESİNE SAHİP OLMALIDIR.

- MAKİNELER İMHA ETMİŞ OLDUKLARI KAĞIDI NAYLON TORBALARA DOLDURMALIDIR. TORBA KOLAY TAKILABİLİR VE ÇIKARILABİLİR BİR MEKANİZMAYA SAHİP OLMALIDIR.

- MAKİNENİN AĞIRLIĞI EN FAZLA  35  KG OLMALIDIR

- MAKİNE BOYUTU ESTETİK AÇIDAN BURO ORTAMINA UYGUNLUK SAĞLAYACAK BİÇİMDE EN AZ  W:58, D:35, H:85 CM ÖLÇÜLERİNDE OLMALIDIR .

- MAKİNENİN MOTORUNUN ISINMAMASI İÇİN HAVALANDIRMA SİSTEMİ OLMALIDIR.

- MOTOR İÇERİSİNDE BULUNAN ANA DİŞLİ ÇELİKTEN OLMALIDIR VE DİŞLİLERİ ÇEVİREN MEKANİZMA ZİNCİRDEN YAPILMIŞ SUPER POTANSİYEL GÜÇ ÜNİTESİNE SAHİP OLMALIDIR.

- MAKİNA TEKERLEK ÜZERİNE MONTAJ EDİLMİŞ KABİN ŞEKLİNDE OLMALIDIR.

- MAKİNE ULUSLAR ARASI ISO  KALİTE BELGESİNE SAHİP OLMALIDIR.

- MAKİNE AVRUPA ÜYE ÜLKELERİNDEN BİRİNİN ÜRETİMİ VEYA TÜRK MALI OLMALIDIR.

- MAKİNE TEKER TEKER KREDİ KARTIDA İMHA EDEBİLMELİDİR.

- FİBER OPTİK SİSTEMİ İLE ENERJİ SMART ÖZELLİĞİNE SAHİP OLMALIDIR.

THE TECHNICAL SPECIFICATION OF KOBRA 260 CC4 PAPER SHREDDER

- THE CUTTING BLADES MUST BE MADE FROM PRIVATELY HARDENED STEEL AND THEY MUST BE UNAFFECTED BY STAPLES, PINS AND  CLIPS.

- THE DOCUMENTS WHICH WERE GIVEN MISTAKENLY MUST BE TAKEN BACK WITH REVERSE BUTTON.

- THE MACHINE MUST START/STOP AUTOMATICLY THROUGH ELECTRONIC EYES WITH STAND-BY FUNCTION AND HAVE A SYSTEM SAVES ENERGY.

- THE HOUSING AND THE STORE OF THE MACHINE MUST BE METAL WHEREAS THE ENGINE BONNET PARTS MUST BE MADE FROM HARD PLASTIC, AESTETIC AND MUST REDUCE THE SOUND DURING THE OPERATION.

- THE VOLTAGE OF THE MACHINE IS 230 AND IT HAS TWO MOTORS WHICH HAVE 2X460 WATT POWER.

- CUTTING SIZES OF THE PAPERS MUST BE 3,5 X 30 MM AND CROSS-CUT

- THE MACHINE MUST SHRED AT LEAST 22/24 SHEETS (A4 70GR/M2) AT A TIME.

- THE NOISE LEVEL MUST BE MAXIMUM 61 dba

- WASTE BAG VOLUME OF THE MACHINE MUST BE 65 LT.

- THE THROAD WIDTH MUST BE AT LEAST 260 MM

- THE SECURITY LEVEL OF THE MACHINE MUST BE AT LEAST AT 3 DIN STANDARD.

- THE MACHINE MUST SHRED HARD ITEMS SUCH AS; CD ROM, FLOPPY DISC, CREDIT CARD, TYPEWRITER RIBBON, AND FILM STRIP.

- THE MACHINE MUST STOP AUTOMATICALLY WHEN ITS DOOR IS OPENED.

- THE MACHINE MUST STOP AUTOMATICALLY WITH A WARNING LIGHT SIGNAL WHEN THE WASTE BAG IS FULL.

- THE ENGINE SPEED MUST BE 0,07 M/SEC. AND IT MUST HAVE THE CAPACITY OF 24 HOURS CONTINUOUS DUTY.

- THE MACHINE MUST SEND THE SHREDDED MATERIALS TO THE PLASTIC BAG.

- THE MAXIMUM WEIGHT OF THE MACHINE MUST BE 35 KG.

- THE DIMENSIONS OF THE MACHINE REGARDING THE AESTETIC APPEARANCE MUST BE AT LEAST 43X31X70 CM IN ORDER TO SUIT TO THE OFFICE CONDITIONS.

- THE MACHINE MUST HAVE A VENTILATION SYSTEM IN ORDER TO AVOID OVERHEATING OF THE ENGINE.

- THE MAIN GEAR IN THE ENGINE MUST BE STEEL AND THE MECHANISM WHICH ROTATES THE GEARS MUST HAVE A SUPER POTANTIAL POWER UNIT WHICH IS MADE FROM CHAIN.

- THE MACHINE MUST BE CABINET WHICH IS MOUNTED TO THE WHEELS.

- THE MACHINE MUST HAVE THE ISO QUALITY CERTIFICATE

- THE MACHINE MUST BE THE PRODUCTION OF A COUNTRY WHICH IS A MEMBER OF EUROPEAN CONTRIES.