PARTS LIST

MICROWAVE OVEN

###### 220V 50Hz

### TECHNICAL DATA

#### Model reference                MG1770M

Functions                      Grill

Oven type                     WD700J-917

Colour                        White

Cavity Volume                  17liter

Supply voltage                  220V 50Hz

Frequency                      2450 MHz±50 MHz

Rated Power Consumption(after 15mins.)

Microwave                      1080W±10%

Microwave output                700W

Grill                           1000W+5/-10%

Rated current(after 15mins.)

Microwave                       5.10A±10%

Grill                            4.40A+5/-10%

###### Safety devices

Thermal protector for magnetron /cavity fire  open at 120ºC

Fuse                            Ceramic type 8A

Primary interlock switch

Second interlock switch

Monitor interlock switch

Control                         Manual

##### Unit dimensions                  458 x 375 x296

Oven cavity size                  320 x 288 x 183

Net Weight                      15.5Kg

Power cord length                 1200mm

Plug                            EURO

| Supplier | Jens Parts No | Code | Pos.No | Order Part No | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A04 |  | 1 |  | Cabinet | 1 |  |
| JENS | B04 |  | 2 |  | Special Screw | 1 |  |
| JENS | B05 |  | 3 |  | Screw | 5 |  |
| JENS | A30 |  | 4 |  | Wire Buckle | 1 |  |
| JENS | A02 |  | 5 |  | Grill Cavity | 1 |  |
| JENS | W02 |  | 6 |  | Gear Motor | 1 |  |
| JENS | B02 |  | 7 |  | Screw | 1 |  |
| JENS | B08 |  | 8 |  | Screw | 1 |  |
| JENS | A37 |  | 9 |  | Splash-Proof board | 1 |  |
| JENS | A36 |  | 10 |  | Special Washer | 1 |  |
| JENS | A35 |  | 11 |  | Turntable Shaft | 1 |  |
| JENS | A33 |  | 12 |  | Roller | 1 |  |
| JENS | A32 |  | 13 |  | Glass Tray | 1 |  |
| JENS | W17 |  | 14 |  | Thermostat,120ºC | 1 |  |
| JENS | B07 |  | 15 |  | Screw | 1 |  |
| JENS | A38 |  | 16 |  | Up Bearing | 1 |  |
| JENS | B01 |  | 17 |  | Screw | 1 |  |
| JENS | A31 |  | 18 |  | Insulated Film | 1 |  |
| JENS | B03 |  | 19 |  | Screw | 4 |  |
| JENS | W24 |  | 20 |  | Heater | 2 |  |
| JENS | A43 |  | 21 |  | Heater Support | 2 |  |
| JENS | B2 |  | 22 |  | Screw | 3 |  |
| JENS | A42 |  | 23 |  | Thermostat Support | 1 |  |
| JENS | A49 |  | 24 |  | Warning Label | 1 |  |
| JENS | A41 |  | 25 |  | Small Sponge Gasket | 1 |  |
| JENS | A45 |  | 26 |  | Prevent Wind Board | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No. | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | B04 |  | 1 |  | Special Screw | 2 |  |
| JENS | W23 |  | 2 |  | Noise Filter | 1 |  |
| JENS | W13 |  | 3 |  | Blower Motor | 1 |  |
| JENS | A27 |  | 4 |  | Space Partition | 1 |  |
| JENS | A28 |  | 5 |  | Fan | 1 |  |
| JENS | W11 |  | 6 |  | Diode Ass’y | 1 |  |
| JENS | W12 |  | 7 |  | HV Fuse | 1 |  |
| JENS | W10 |  | 8 |  | Capacitor 0.92uF | 1 |  |
| JENS | A29 |  | 9 |  | Capacitor Band | 1 |  |
| JENS | W20 |  | 10 |  | Power supply Cord | 1 |  |
| JENS | A26 |  | 11 |  | Duct | 1 |  |
| JENS | B05 |  | 12 |  | Special Screw | 1 |  |
| JENS | W08 |  | 13 |  | Lamp | 1 |  |
| JENS | W09 |  | 14 |  | Lamp Socket | 1 |  |
| JENS | W01 |  | 15 |  | Magnetron | 1 |  |
| JENS | A21 |  | 16 |  | Switch Holder | 1 |  |
| JENS | B01 |  | 17 |  | Special Screw | 4 |  |
| JENS | A24 |  | 18 |  | Small Revolving Arm | 1 |  |
| JENS | W04 |  | 19 |  | Primary Interlock Switch | 1 |  |
| JENS | W05 |  | 20 |  | Door Sensing Switch | 1 |  |
| JENS | W04 |  | 21 |  | Interlock Monitor Switch | 1 |  |
| JENS | A22 |  | 22 |  | Big Revolving Arm | 1 |  |
| JENS | A25 |  | 23 |  | Returning Spring | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No. | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A20 |  | 1 |  | Quake-Proof Cushion | 1 |  |
| JENS | W02 |  | 2 |  | Transformer | 1 |  |
| JENS | A15 |  | 3 |  | Base Board | 1 |  |
| JENS | B01 |  | 4 |  | Special Screw | 4 |  |
| JENS | A19 |  | 5 |  | Gear Motor Cover | 1 |  |
| JENS | B03 |  | 6 |  | Special Screw | 1 |  |
| JENS | B03 |  | 7 |  | Special Screw | 7 |  |
| JENS | A18 |  | 8 |  | Pin | 4 |  |
| JENS | A17 |  | 9 |  | Oven leg | 4 |  |
| JENS | A16 |  | 10 |  | Bottom Hinge | 1 |  |
| JENS | B09 |  | 11 |  | Nut | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A43 |  | 1 |  | Front nameplate | 1 |  |
| JENS | A05 |  | 2 |  | Door Cover | 1 |  |
| JENS | A09 |  | 3 |  | Protection Film | 1 |  |
| JENS | A06 |  | 4 |  | Window Board | 1 |  |
| JENS | A08 |  | 5 |  | Spring | 1 |  |
| JENS | A07 |  | 6 |  | Door latch | 1 |  |
| JENS | A10 |  | 7 |  | Choke Dielectric | 1 |  |
| JENS | B07 |  | 8 |  | Screw | 4 |  |
| JENS | A03 |  | 9 |  | Door Assembly Complete | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No | Description | Q’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | B02 |  | 1 |  | Screw | 4 |  |
| JENS | A12 |  | 2 |  | Time knob | 1 |  |
| JENS | A12 |  | 3 |  | Power knob | 1 |  |
| JENS | A11 |  | 4 |  | Control Frame | 1 |  |
| JENS | W16 |  | 5 |  | Timer | 1 |  |

SW1: TIME CONTROL SWITCH

SW2: POWER CONTROL SWITCH

# SWA: THE PRIMARY INTERLOCK SWITCH

## SWB: THE SECOND INTERLOCK SWITCH

SWC: THE MONITOR INTERLOCK SWITCH

L: OVEN LAMP

T: TIMER MOTOR

MF: FAN MOTOR

MT: TRAY MOTOR

H: HEATER

FU1,FU2: THERMOSTAT

F1,F2: FUSE