PARTS LIST

MICROWAVE OVEN

###### 220V 50Hz

### TECHNICAL DATA

#### Model reference                MS1770M

Oven type                     WP700J-917

Colour                        White

Cavity Volume                  17liter

Supply voltage                  220V 50Hz

Frequency                      2450 MHz±50 MHz

Rated Power Consumption (after 15mins.)

Microwave                      1080W±10%

Microwave output                700W

Rated current (after 15mins.)

Microwave                      5.10A±10%

Safety devices

Thermal protector for magnetron     open at 160ºC

Thermal protector for cavity fire     open at 105ºC

Fuse                            Ceramic type 8A

Primary interlock switch

Second interlock switch

Monitor interlock switch

Control                         Manual

##### Unit dimensions                  458 x 375 x296

Oven cavity size                  320 x 288 x 183

Net Weight                      15.5Kg

Power cord length                 1200mm

Plug                            EURO

| Supplier | Jens Part No | Code | Pos.No | Order Part No | Description | Q’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A04 |  | 1 |  | Cabinet | 1 |  |
| JENS | B04 |  | 2 |  | Special Screw | 1 |  |
| JENS | B05 |  | 3 |  | Screw | 5 |  |
| JENS | A30 |  | 4 |  | Wire Buckle | 1 |  |
| JENS | A01 |  | 5 |  | Cavity | 1 |  |
| JENS | W02 |  | 6 |  | Gear Motor | 1 |  |
| JENS | B02 |  | 7 |  | Screw | 1 |  |
| JENS | B08 |  | 8 |  | Screw | 1 |  |
| JENS | A37 |  | 9 |  | Splash-Proof board | 1 |  |
| JENS | A36 |  | 10 |  | Special Washer | 1 |  |
| JENS | A35 |  | 11 |  | Turntable Shaft | 1 |  |
| JENS | A33 |  | 12 |  | Roller | 1 |  |
| JENS | A32 |  | 13 |  | Glass Tray | 1 |  |
| JENS | W17 |  | 14 |  | Thermostat,105ºC | 1 |  |
| JENS | B07 |  | 15 |  | Screw | 1 |  |
| JENS | A38 |  | 16 |  | Up Bearing | 1 |  |
| JENS | B01 |  | 17 |  | Screw | 1 |  |
| JENS | A31 |  | 18 |  | Insulated Film | 1 |  |
| JENS | B03 |  | 19 |  | Screw | 1 |  |

| Supplier | Jens Part No | Code | PosNo | Order Part No. | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | B04 |  | 1 |  | Special Screw | 2 |  |
| JENS | W23 |  | 2 |  | Noise Filter | 1 |  |
| JENS | W13 |  | 3 |  | Blower Motor | 1 |  |
| JENS | A27 |  | 4 |  | Space Partition | 1 |  |
| JENS | A26 |  | 5 |  | Fan | 1 |  |
| JENS | W11 |  | 6 |  | Diode Ass’y | 1 |  |
| JENS | W12 |  | 7 |  | HV Fuse | 1 |  |
| JENS | W10 |  | 8 |  | Capacitor 0.92uF | 1 |  |
| JENS | A29 |  | 9 |  | Capacitor Band | 1 |  |
| JENS | W20 |  | 10 |  | Power supply Cord | 1 |  |
| JENS | A26 |  | 11 |  | Duct | 1 |  |
| JENS | B05 |  | 12 |  | Special Screw | 1 |  |
| JENS | W08 |  | 13 |  | Lamp 250V 20W | 1 |  |
| JENS | W09 |  | 14 |  | Lamp Socket | 1 |  |
| JENS | W01 |  | 15 |  | Magnetron | 1 |  |
| JENS | W19 |  | 16 |  | Thermostat 160ºC | 1 |  |
| JENS | B07 |  | 17 |  | Special Screw | 2 |  |
| JENS | A24 |  | 18 |  | Small Revolving Arm | 1 |  |
| JENS | W04 |  | 19 |  | Primary Interlock Switch | 1 |  |
| JENS | W05 |  | 20 |  | Door Sensing Switch | 1 |  |
| JENS | W04 |  | 21 |  | Interlock Monitor Switch | 1 |  |
| JENS | A22 |  | 22 |  | Big Revolving Arm | 1 |  |
| JENS | A25 |  | 23 |  | Returning Spring | 1 |  |
| JENS | A21 |  | 24 |  | Switch Holder | 1 |  |
| JENS | B01 |  | 25 |  | Special Screw | 4 |  |

| Supplier | Jens Part No | Code | PosNo | Order Part No. | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A20 |  | 1 |  | Quake-Proof Cushion | 1 |  |
| JENS | W02 |  | 2 |  | Transformer | 1 |  |
| JENS | A15 |  | 3 |  | Base Board | 1 |  |
| JENS | B01 |  | 4 |  | Special Screw | 4 |  |
| JENS | A19 |  | 5 |  | Gear Motor Cover | 1 |  |
| JENS | B03 |  | 6 |  | Special Screw | 1 |  |
| JENS | B03 |  | 7 |  | Special Screw | 7 |  |
| JENS | A18 |  | 8 |  | Pin | 4 |  |
| JENS | A17 |  | 9 |  | Oven leg | 4 |  |
| JENS | A16 |  | 10 |  | Bottom Hinge | 1 |  |
| JENS | B09 |  | 11 |  | Nut | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No | Description | O’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | A43 |  | 1 |  | Front nameplate | 1 |  |
| JENS | A05 |  | 2 |  | Door Cover | 1 |  |
| JENS | A09 |  | 3 |  | Protection Film | 1 |  |
| JENS | A06 |  | 4 |  | Window Board | 1 |  |
| JENS | A08 |  | 5 |  | Spring | 1 |  |
| JENS | A07 |  | 6 |  | Door latch | 1 |  |
| JENS | A10 |  | 7 |  | Choke Dielectric | 1 |  |
| JENS | B07 |  | 8 |  | Screw | 4 |  |
| JENS | A03 |  | 9 |  | Door Assembly Complete | 1 |  |

| Supplier | Jens Part No | Code | Pos.No | Order Part No | Description | Q’ty |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| JENS | B02 |  | 1 |  | Screw | 4 |  |
| JENS | A12 |  | 2 |  | Time knob | 1 |  |
| JENS | A12 |  | 3 |  | Power knob | 1 |  |
| JENS | A11 |  | 4 |  | Control Frame | 1 |  |
| JENS | W16 |  | 5 |  | Timer | 1 |  |

SW1: TIME CONTROL SWITCH

SW2: POWER CONTROL SWITCH

# SWA: THE PRIMARY INTERLOCK SWITCH

## SWB: THE SECOND INTERLOCK SWITCH

SWC: THE MONITOR INTERLOCK SWITCH

L: OVEN LAMP

T: TIMER MOTOR

FM: FAN MOTOR

TM: TRAY MOTOR

FU1, FU2: THERMOSTAT

F1, F2: FUSE