##### MicroMAPS: From Storage to Flight

AOE 4066: Aircraft and Space Design

Department of Aerospace and Ocean Engineering

Virginia Polytechnic Institute and State University

5 May 2003

Team Members

| Adam Dubinskas Conor Haines Rivers Lamb Jennifer Lin Lee McCoy Shan Mohiuddin | Christopher Nickell Monsid Poovantana Binh Tran Mike Tuttle Whitney Waldron Josh Zhou |
| --- | --- |

Table of Contents

List of Figures	vii

List of Tables	x

List of Acronyms	xii

Chapter 1: Introduction and Problem Definition	1

1.1 MicroMAPS Information	1

1.1.1 MicroMAPS History	1

1.1.2 MicroMAPS Science Mission	2

1.1.3 MAPS History	2

1.1.4 MicroMAPS Physical Characteristics	3

1.1.5 Descriptive Scenario	4

1.2 Problem Definition	4

1.2.1 Assessment of Scope	5

1.2.2 Required Disciplines	5

1.2.3 Societal Sectors and Actors Involved	6

1.2.4 Relevant and Subjective Elements	6

1.3 Needs, Alterables, and Constraints	6

1.3.1 Proteus Mission Needs, Alterables, and Constraints	7

1.3.2 Dedicated Aircraft Needs, Alterables, and Constraints	8

1.3.3 Dedicated Spacecraft Needs, Alterables, and Constraints	9

1.4 Summary	10

Chapter 2: Value System Design	11

2.1 Proteus Objectives	11

2.1.1 Maximization of Performance	11

2.1.2 Minimization of Cost	13

2.2 Dedicated Aircraft Objectives	14

2.2.1 Maximization of Performance	14

2.2.2 Minimization of Cost	16

2.3 Dedicated Spacecraft Objectives	17

2.3.1 Maximization of Performance	17

2.3.2 Minimization of Cost	20

2.4 Summary	21

Chapter 3: Proteus	22

3.1 Mission Overview	22

3.2 Power	23

3.2.1 System Overview	23

3.2.2 Main Power Converter NB50S41	26

3.2.3 PC104 Power Supply CB5S8	29

3.2.4 Triple Output MicroMAPS Power Supply NB45T41	30

3.2.5 EMI Filter NBF5041	32

3.2.6 Heat Dissipation	34

3.2.7 Wires, Connectors, and Line Diagram	34

3.3 Data Acquisition	37

3.3.1 Computer55	37

3.3.2 CPU Board	37

3.3.3 Power Board	38

3.3.4 PC104 Enclosure	40

3.3.5 System Setup	41

3.4.1 1-Wire® Network14	42

3.4.2 1-Wire® Serial Interface35	44

3.4.3 Thermal Compound	45

3.5 Structure	45

3.5.1 Systems and Weights	46

3.5.2 MicroMAPS Viewing Window	50

3.5.3 Instrument Suite Mounting Platform	51

3.5.4 Installation and Configuration	53

4.1 Introduction	55

4.2 Aircraft RFP	55

4.3 Selection of Final Design Concept	59

4.3.1 Menelaus I	59

4.3.2 Menelaus II	60

4.3.3 The Decision and Suggested Changes	61

4.4 Detailed Sizing	63

4.4.1 Sizing Process	64

4.4.2 Sizing Results	69

4.5 Propulsion	69

4.5.1 System Requirements	69

4.5.2 Engine Selection	70

4.5.3 FJ44 Performance Characteristics	72

4.5.4 Engine Ducting	73

4.4.5 System Maintenance	74

4.6 Aerodynamics	74

4.6.1 Configuration Design	75

4.6.2 Airfoils	77

4.6.3 Computational Aerodynamic Analysis	82

4.7 Stability and Control	87

4.7.1 Justification of Configuration Geometry	87

4.7.2 Static Margin	89

4.7.3 Control Surface Sizing	92

4.8 Performance	95

4.8.1 Mission Profile Analysis	95

4.8.2 Aircraft Comparison	97

4.9.1 Materials	98

4.9.2 V-n Diagram	100

4.9.3 Wing Elements	100

4.9.4 Fuselage	101

4.9.5 Tail Booms	103

4.9.6 Weights Breakdown	103

4.9.7 Center Of Gravity Travel	104

4.10 Systems	104

4.10.1 General Layout	104

4.10.2 Payload System	105

4.10.3 Fuel System	106

4.10.4 Landing Gear	106

4.10.5 Communication	106

4.10.6 Avionics	107

4.10.6 Flight Controls	107

4.11 Cost Analysis	107

4.12 Final Proposal	109

Chapter 5: Aiolos	112

5.1 Orbit Design	112

5.1.1 Specialized Orbits	112

5.1.2 Propulsion	113

5.1.3 Altitude	114

5.1.4 Inclination	116

5.1.5 Orbit Determination System	117

5.2 Attitude Determination and Control System (ADCS)	118

5.2.1 Control Modes	119

5.2.2 Attitude Determination Components	119

5.2.3 Disturbance Torques	122

5.2.4 Attitude Control Components	124

5.3 Power	126

5.3.1 Operating Conditions and Requirements	127

5.3.2 Power Generation	128

5.3.3 Energy Storage	131

5.4 Command and Data Handling (C&DH)	132

5.5 Communication	133

5.5.1 Antenna	133

5.5.2 Transmitter	134

5.5.3 Receiver	135

5.6 Thermal Management	136

5.6.1 Temperature Limits	136

5.6.2 Heat Sources	137

5.6.3 Radiator	138

5.6.4 Multi-Layered Insulation	140

5.7 Launch Vehicle	141

5.7.1 Cost Comparison	142

5.7.2 Athena II	142

5.7.3 Delta II	145

5.7.4 Taurus	147

5.7.5 Comparison of Options	150

5.8 Structures	151

5.9 Cost Analysis	157

5.10 Spacecraft Summary	157

References	158

# List of Figures

Frontispiece: The Proteus Aircraft in Flight49

Figure 1: The MicroMAPS Instrument34	4

Figure 2: MicroMAPS power supply chassis10	26

Figure 3: NB50S Main Converter Schematic41	28

Figure 4: CB5S PC104 Power Supply Diagram8	30

Figure 5: NB45T MicroMAPS Power Supply41	32

Figure 6: NBF50 EMI Filter Diagram41	33

Figure 7: Power System Connection Diagram	36

Figure 8: MZ104+ Mechanical Specifications55	38

Figure 9: CT104 Enclosure – 6 inch depth55	40

Figure 10: DS18S20 1-Wire® Digital Temperature Sensor14	43

Figure 11: HMP-2001S Digital Humidity Sensor (left) and	44

Figure 12: TEMP05 1-Wire® Serial Interface35	45

Figure 13: PC104 Exterior Casing and Mounting Base (all dimensions in inches)	47

Figure 14: MicroMAPS Diagram (inches)	48

Figure 15: NBF50 Diagram (inches)	48

Figure 16: CB5S Diagram (inches)	49

Figure 17: NB50S Diagram (inches)	49

Figure 18: MicroMAPS Power Supply Diagram (inches)	49

Figure 19: External Pod Diagram	50

Figure 20: Base Platform Diagram, 6061-T6 Aluminum (inches)	51

Figure 21: Pod Mounting Configuration10	52

Figure 22: Endurance Mission Profile	59

Figure 23: Menelaus I	60

Figure 24: Menelaus II	61

Figure 25: New Configuration, Including Changes Developed in Decision Process	64

Figure 26: Constraints Diagram to Optimize T/W and W/S	68

Figure 27: FJ44-1A Propulsion System62	71

Figure 28: FJ44-1A Variant Properties62	71

Figure 29: Net Thrust and SFC for FJ44 Variant	72

Figure 30: Take-off Thrust under Varying Conditions	73

Figure 31: The Main Wing Airfoil - NASA/Langley/Whitcomb LS(1)-0417 (GA(W))57	78

Figure 32: The Tail Surface Airfoil - NACA 64-01257	79

Figure 33: Main Wing Thickness-to-Chord Ratio and Wing Fuel Capacity	80

Figure 34: Results from Boundary Layer Analysis	82

Figure 35: Model Layout and Pressure Distribution in Tornado	84

Figure 36: Numerical Data Generated by Tornado Iterations (all forces in Newtons)	85

Figure 37: Span Loading Generated by Tornado	86

Figure 38: Detail of the A-tail and Communications Pod	88

Figure 39: Illustration of Roll-Yaw Coupling	89

Figure 40: Tornado-Generated Stability Derivatives	91

Figure 41: Perseus B Aileron Size and Location39	92

Figure 42: Menelaus Aileron Size and Location (all dimensions in ft)	93

Figure 43: Predator B Ruddervator Size and Location39	94

Figure 44: Menelaus Ruddervator Size and Location (all dimensions in ft)	94

Figure 45: Optimal Mission Profile	96

Figure 46: V-n Diagram	100

Figure 47: Wing Structure	101

Figure 48: Fuselage Structure	102

Figure 49: Nose Cone Connection	102

Figure 50: Center of Gravity Travel	104

Figure 51: General Layout of Systems	105

Figure 52: Landing Gear Arrangement (dimensions in ft)	106

Figure 53: Percentage of RDT&E Cost	108

Figure 54: Menelaus Three-View	111

Figure 55: World Population Density63	116

Figure 56: SGR-20 Receiver and Antennas48	118

Figure 57: Ithaco Conical Earth Sensor4	120

Figure 58: Surrey Two Axis Sun Sensor48	121

Figure 59: Ithaco IM-1034	122

Figure 60: Ithaco Type A and B Wheels4	125

Figure 61: Ithaco Magnetic Torquers4	126

Figure 62: S-band Quadrifilar Helix Antenna Footprint48	134

Figure 63: Athena II Launch Vehicle3	143

Figure 64 Athena II Performance28	144

Figure 65: Athena II Payload Fairing28	144

Figure 66: Delta II Launch Vehicle Family15	145

Figure 67: Delta II Launch Vehicle15	146

Figure 68: Delta II 7920 Performance28	146

Figure 69: Delta II Payload Fairings15	147

Figure 70: Taurus Launch Vehicle Family30	148

Figure 71: Taurus Launch Vehicle30	148

Figure 72: Taurus Performance28	149

Figure 73: Taurus Payload Fairing30	149

Figure 74: MicroMAPS Location within Aiolos	155

Figure 75: Complete Aiolos Configuration	156

# List of Tables

Table 1: MicroMAPS Physical Characteristics59	3

Table 2: General Needs, Alterables, and Constraints	7

Table 3: Proteus Mission Needs, Alterables, and Constraints	8

Table 4: Dedicated Aircraft Needs, Alterables, and Constraints	9

Table 5: Dedicated Spacecraft Needs, Alterables, and Constraints	9

Table 6: Proteus Performance Objectives	13

Table 7: Proteus Cost Objectives	14

Table 8: Dedicated Aircraft Performance Objectives	16

Table 9: Dedicated Aircraft Cost Objectives	17

Table 10: Dedicated Spacecraft Performance Objectives	20

Table 11: Dedicated Spacecraft Cost Objectives	21

Table 12: Military Electrical Standards8	24

Table 13: NB50S Main Converter Details41	28

Table 14: CB5S PC104 Power Supply Details8	29

Table 15: NB45T MicroMAPS Power Supply Details41	31

Table 16: NBF50 EMI Filter Details41	33

Table 17: Heat generation	34

Table 18: Electrical and Mechanical specifications of the HE10455	39

Table 19: The Decision Matrix	62

Table 20: Estimation of CL	65

Table 21: Wing Loading and Span Loading	65

Table 22: TOGW for Turbofan and Turboprop	66

Table 23: TOGW Estimated from Existing Aircraft	66

Table 24: Aspect Ratio Estimation	67

Table 25: Thrust-to-Weight Ratio	67

Table 26: Results of Aircraft Sizing Process	69

Table 27: Initial Engine Candidates62	70

Table 28: The Results from Friction Analysis for the Shortened Aircraft	77

Table 29: Input Data for Boundary Layer Analysis	81

Table 30: Final Aerodynamic Properties	87

Table 31: Menelaus Comparison	97

Table 32: Approximate Material Cost58	99

Table 33: Weight Summary	103

Table 34: Breakdown of RDT&E Cost Analysis	108

Table 35: Comparison with RFP	109

Table 36: Atmospheric Densities at Minimum Solar Activity 61	115

Table 37: Orbital Decay Calculations	115

Table 38: SGR-10 Data48	118

Table 39: Ithaco Conical Earth Sensor Specifications4	120

Table 40: Surrey Sun Sensor Specifications48	121

Table 41: Ithaco IM-103 Specifications4	122

Table 42: Disturbance Torque Equations Variable Definition	123

Table 43: Disturbance Torque Calculations	124

Table 44: Attitude Actuator Calculations	125

Table 45: Ithaco Wheel TW-16B32 Specifications4	125

Table 46: Ithaco Magnetic Torquer TR30CFN Specifications4	126

Table 47: Subsystem Power Requirements	128

Table 48: Spectrolab Triple Junction Solar Cell Information56	129

Table 49: SAFT Lithium Ion Battery Information32	131

Table 50: Operational Temperature Limit	137

Table 51: Environmental Fluxes in Space23	138

Table 52: Internal Power Dissipation	138

Table 53: Thermal Calculation Variables and Definitions	140

Table 54: Launch Vehicle Cost Analysis61	142

Table 55: Launch Vehicle Selection Criteria3,15,28,30	150

Table 56: Ranking of Launch Vehicles	151

Table 57: Aluminum 7075-T73 Material Properties	152

Table 58: Launch Vehicle Structural Impact	153

Table 59: Launch Vehicle Dynamic Impact	154

Table 60: Subsystem Mass Summation	155

Table 61: Inertia Calculations	156

Table 62: Cost Analysis	157

# List of Acronyms

AC		Alternating Current

ADCS		Attitude Determination and Control System

BOL		Beginning of Life

C&DH		Command and Data Handling

CES		Conical Earth Sensor

CG		Center of Gravity

CO		Carbon Monoxide

DARCO	Defense Airborne Reconnaissance Office

DC		Direct Current

DoD		Department of Defense

DOD		Depth of Discharge

EMI		Electromagnetic Interference

EOL		End of Life

ERAST	Environmental Research Aircraft and Sensor Technology

FAA		Federal Aviation Administration

GPS		Global Positioning System

GTO		Geosynchronous Transfer Orbit

HPA		High Power Amplifier

IR		Infrared

KLC		Kodiak Launch Complex

KSC		Kennedy Space Center

KTAS		Knots True Airspeed

LaRC		Langley Research Center

LELR		Long Endurance Long Range

LEO		Low Earth Orbit

MAPS		Measurement of Air Pollution from Space

MLI		Multi-Layer Insulation

NASA		National Aeronautics and Space Administration

OH		Hydroxyl Radical

OSR		Optical Solar Reflectors

R&D		Research and Development

RAM		Random Access Memory

RFP		Request for Proposal

ROM		Read Only Memory

SGR		Space GPS Receivers

SSLV		Standard Small Launch Vehicle

SSTI		Small Spacecraft Technology Initiative

SSTL		Surrey Satellite Technology Ltd.

STS		Space Shuttle Transportation System

TDRS		Tracking and Data Relay Satellite

TFU		Theoretical First Unit

TOGW		Takeoff Gross Weight

UAV		Unmanned Aerial Vehicle

VAFB		Vandenberg Air Force Base

VSGC		Virginia Space Grant Consortium

W/S		Wing Loading

# Chapter 1: Introduction and Problem Definition

The problem definition portion of the report provides background information for the problem at hand.  In addition, it sets the guidelines for the design process and the requirements for the mission analyses that are completed.  The establishment of these goals leads to a more effective and efficient design process.  This problem definition includes basic information on the MicroMAPS instrument, a problem definition, and the needs, alterables, and constraints of the mission.

## 1.1 MicroMAPS Information

Originally flown on the Space Shuttle in 1981, the MAPS (Measurement of Air Pollution from Satellites) instrument measured carbon monoxide levels in the troposphere59.  The MicroMAPS project was intended to be a longer duration, cheaper solution meant to enhance the previous scientific results.59  Originally it was intended for use on the Clark spacecraft, which was cancelled in 1998 as discussed below.  Currently, researchers at the National Aeronautics and Space Administration’s (NASA) Langley Research Center (LaRC) are interested in flying the MicroMAPS instrument on the Proteus research aircraft.  The work of this design team includes designing the instrument interface with the Proteus.  In addition, dedicated aircraft and spacecraft are designed for the MicroMAPS instrument, resulting in a final comparison between the three options.24

### 1.1.1 MicroMAPS History

In February 1998, NASA made the decision to terminate the Clark spacecraft because of mission costs, launch schedule delays, and concerns over on-orbit capabilities.40  As part of the Small Spacecraft Technology Initiative (SSTI), this mission was intended to demonstrate several advanced spacecraft technologies and included several instruments.10  One of the instruments included was the MicroMAPS Gas Filter Correlation Radiometer (MicroMAPS).  This instrument has since been maintained at NASA Langley, where it has recently undergone testing and will soon be recalibrated for flight in the Proteus research aircraft.24

### 1.1.2 MicroMAPS Science Mission

The science goal of the MicroMAPS instrument is to learn about the chemical and transport processes in the troposphere of the Earth.  This increased knowledge of conditions in the atmosphere would benefit science by improving the understanding of the changes in the atmosphere related to tropospheric composition, climate, and stratospheric composition.  These topics would lead to the creation of strategies for sustainable development and resource allocation for the Earth.59

The ultimate goal of the MicroMAPS science mission is to use remote sensing of tropospheric carbon monoxide (CO) to understand the sources, sinks, transport, and distribution of CO in the troposphere.  Carbon monoxide is the major consumer of the hydroxyl (OH) radical, a major oxidizer of reduced species.  Reduced species are often radiatively active and contribute to changes in the planetary heat balance.  Hence, increased CO emissions generally correspond to increases in the concentrations of radiatively or chemically active gases.59

### 1.1.3 MAPS History

The original version of MicroMAPS was the MAPS experiment that flew aboard NASA’s Space Shuttle Transportation System (STS) during four short flights: November 1981, October 1984, April 1994, and October 1994.  Whereas this data has been valuable in establishing the variations of CO distributions, these missions had a maximum duration of 10 days and a latitude range of ( 57°.  MicroMAPS was designed to be a smaller and cheaper instrument that could collect global data with a lifetime goal of at least a year.  This information would improve the understanding of CO variations from season to season and across variations in location.59

### 1.1.4 MicroMAPS Physical Characteristics

Since the MicroMAPS instrument is already constructed, the physical properties and operational requirements of the device are well known.  Table 1 displays these characteristics which must be taken into account for each design scenario, be it a dedicated spacecraft, a dedicated aircraft, or the Proteus research vessel.  A picture of the actual MicroMAPS instrument is supplied below in Figure 1.

Table 1: MicroMAPS Physical Characteristics59

| Characteristic | Metric Units | English Units |
| --- | --- | --- |
| Length | 0.254 m | 10 in |
| Width | 0.17145 m | 6.75 in |
| Height | 0.14605 m | 5.75 in |
| Mass | 6.4 kg | 14 lb |
| Lens Tube Length | 0.0762 m | 3.0 in |
| Operating Temperature | 273-298 K | 0 – 25 °C |
| Power Consumption | 24 (max) W | 1.364 Btu/min |
| Telescope Aperture | 0.02032 m | 0.8 in |
| Square Telescope FOV | 137.5099 rad | 2.4° |
| Gas Cell Clear Aperture | 0.02032 m (circular) | 0.8 in (circular) |
| Beam Size at Gas Cell Chopper | 0.00508 m (square) | 0.2 in (square) |
| Input Voltages | 15, -15, 5 V |  |
| Operating Humidity Levels | 30-50% |  |
| Data From Chopper and Telemetry Acquisition Rate | 42.6 bytes/s |  |

Figure 1: The MicroMAPS Instrument34

### 1.1.5 Descriptive Scenario

Successful implementation of the MicroMAPS instrument would be a tremendous science asset.  Whether onboard an aircraft or a spacecraft, this instrument would be able to record vital information about carbon monoxide emissions and the transport processes that are interrelated.  This information is important in contributing to the understanding of the Earth as a system.  Scientists are likely to use this information both for confirming other data as well as for the data itself.

## 1.2 Problem Definition

Due to the cancellation of the Clark spacecraft explained above, scientists at LaRC have been searching for alternative platforms for MicroMAPS.  While the decision has been made to use the Proteus research aircraft, there is interest in comparing this option to the dedicated aircraft and spacecraft options.  This section outlines the goals of these three projects.

### 1.2.1 Assessment of Scope

The nature of the upcoming MicroMAPS mission requires that the first priority be the successful integration of the instrument into the Proteus aircraft.  This portion of the project requires a thorough understanding of the characteristics of Proteus and the development of an interface between the instrument and the aircraft.  As such, the first task is to design the structure and the subsystems required so that MicroMAPS can be operated while flying onboard Proteus.  A similar interface may be used for the design of the dedicated aircraft and spacecraft.  These two vehicles are designed specifically for the MicroMAPS instrument and include all of the appropriate subsystems design and analysis.  These complete designs allow for a performance and cost comparison of the three options.

### 1.2.2 Required Disciplines

The scope as explained here involves many disciplines.  Knowledge of atmospheric sciences is required for an understanding of how MicroMAPS will behave in varying atmospheric conditions on the three possible platforms.  Detailed electrical and computer engineering work is necessary for development of the interface between Proteus and MicroMAPS as well as the systems such as communications and command and data handling on both the aircraft and spacecraft.  In addition, a range of disciplines is required for the final designs: mission planning, trajectory analysis, aerodynamics, stability and control, performance, structural design, power analysis, thermal management, and project management.  Aerospace engineering students in the aircraft and spacecraft design classes at Virginia Tech fill these roles.

### 1.2.3 Societal Sectors and Actors Involved

During this process, the engineering students at Virginia Tech have to interact with other organizations and must consider the impact of design decisions.  Contact with NASA is vital to understand the science goals and restrictions of the MicroMAPS instrument.  While other interactions with the agency are necessary, the primary contact is LaRC, the center responsible for the instrumentation for atmospheric science data.  International laws must be upheld in all three MicroMAPS scenarios.  Finally, public safety is of paramount importance for the decisions made in planning these missions.

### 1.2.4 Relevant and Subjective Elements

As mentioned previously, the top priority for this project is to complete the design of the structure that allows MicroMAPS to be integrated with the Proteus research aircraft.  This portion of the project is restrictive, as the existing MicroMAPS instrument and the Proteus aircraft dictate the decisions that are made.  Some of the subjective elements include the flight profile and the configuration of the Proteus and the method by which MicroMAPS stores and transmits data.

The dedicated aircraft and spacecraft allow for a considerable amount of flexibility.  The primary goal for these two missions is basic: to conduct a science mission using the MicroMAPS instrument.  Completion of this goal requires a thorough subsystem design and overall analysis of each mission.  These decisions are left to the design team and are reached after weighing the implications on the cost and performance for each case.

## 1.3 Needs, Alterables, and Constraints

Each platform option has slightly different requirements for the MicroMAPS instrument based on the interface, vehicle, and nature of the operating environment. One way to analyze these requirements is through the tabulation of needs, alterables, and constraints.  Compiling such a list provides a better understanding of what the goals are for the project and what aspects can be changed.  The needs category includes a simple definition of the problem; the alterables category includes those considerations that are changed to meet the goals of the mission; and the constraints category includes the guidelines and restrictions that must be met by the mission.  For the MicroMAPS project, there are a few fundamental considerations and aspects which apply to all three scenarios.  This general list of needs, alterables, and constraints is included in Table 2.

Table 2: General Needs, Alterables, and Constraints

| Category | Element |
| --- | --- |
| Needs: | To develop and assess three distinct options for carrying out the science mission for which the MicroMAPS instrument was built |
| Alterables: | Mission profile Material selection |
|  | Method of data acquisition Method of data communication/storage Method of environmental protection |
| Constraints: | Cost Vibration control Structural limits Attitude requirement: ( 2.5( of nadir pointing Attitude knowledge: ( 0.5( of nadir pointing Size and weight of instrument and supporting systems Project lifetime Atmospheric regulation: Relative humidity between 0% and 55% Temperature regulation: 32(F (0(C) and 77(F (25(C) Power requirements: 24 Watts, 5 V and (15 V |

### 1.3.1 Proteus Mission Needs, Alterables, and Constraints

As explained previously, the current plans for the MicroMAPS instrument are for the integration of this device in the Proteus research aircraft.  The role of this team is to design a system to provide an interface between the aircraft and the instrument.  The needs, alterables, and constraints that only apply to this portion of the project are listed in

Table 3.

Table 3: Proteus Mission Needs, Alterables, and Constraints

| Category | Element |
| --- | --- |
| Needs: | To provide an effective operating environment onboard the Proteus aircraft for the MicroMAPS instrument |
| Alterables: | Location of instrument on airframe Vehicle configuration |
| Constraints: | Prevention of contamination and condensation Requirements of other missions on Proteus Proteus’s endurance/range: 14 hours at 500 NM radius (with 12500 lb takeoff weight) Rules and procedures for Proteus flights Power supplied by Proteus: 20 kW (continuous, thermal-managed) |

### 1.3.2 Dedicated Aircraft Needs, Alterables, and Constraints

The Proteus aircraft provides a relatively simple solution to the problem of flying the MicroMAPS instrument, however it may be that this platform is not an optimal aircraft for this device.  An aircraft designed specifically to house this instrument may provide better operating characteristics for the mission.  The needs, alterables, and constraints compiled specifically for the design of a dedicated aircraft are listed in Table 4.

Table 4: Dedicated Aircraft Needs, Alterables, and Constraints

| Category | Element |
| --- | --- |
| Needs: | To design a dedicated aircraft to carry out the science mission of the MicroMAPS instrument |
| Alterables: | Aircraft type Propulsion type Power source Geometric characteristics Support systems design |
| Constraints: | Prevention of contamination and condensation Altitude requirement: 60,000 ft Endurance/range requirement: 40 hours at 1000 NM radius Lifespan of instrument in atmospheric flight conditions FAA compliant |

### 1.3.3 Dedicated Spacecraft Needs, Alterables, and Constraints

Originally designed for the Clark spacecraft, it is reasonable to assume that the MicroMAPS instrument would have the best performance onboard a spacecraft.  Space missions are generally significantly more expensive than aircraft missions, yet the improved performance could be important to this science mission.  The needs, alterables, and constraints for the dedicated spacecraft option are listed in Table 5.

Table 5: Dedicated Spacecraft Needs, Alterables, and Constraints

| Category | Element |
| --- | --- |
| Needs: | To design a dedicated spacecraft to carry out the science mission of the MicroMAPS instrument |
| Alterables: | Orbit design Attitude design (ADCS) Launch vehicle Propulsion type Primary/secondary payload Power source Structure |
| Constraints: | Cleanliness of instrument No violation of international law |

## 1.4 Summary

Chapter 1 gives an introduction to the history of the MicroMAPS instrument.  It explains the top priority of this design team, to design the interface that allows the science mission to be conducted from the Proteus aircraft.  In addition, the dedicated aircraft and spacecraft options are presented, covering the options for comparison in this analysis.  Through the listing of needs, alterables, and constraints, the scope of each scenario is discussed.  The following chapter discusses the value system design, leading to the detailed analysis of each design option.

# Chapter 2: Value System Design

One requirement of the design process is the development of guidelines which are used to optimize the design.  This value system design starts at the top level with two basic objectives: to maximize mission performance and to minimize mission cost.  If these two conditions are met, then the overall design is optimized.  For each subsystem, there are sub-objectives that fall into either the performance or cost categories.  This section presents these sub-objectives for each of the three possible platforms, and the manner in which each objective can be measured.

## 2.1 Proteus Objectives

The Proteus design primarily involves the creation of the interface that supports MicroMAPS in its mission on this research aircraft.  As such, many constraints are already set.  Yet, it is important to provide guidelines and a basis that is used in the analysis and comparison of performance and cost for each possible option.

### 2.1.1 Maximization of Performance

Several subsystems must be optimized to maximize performance of the Proteus-based operation of MicroMAPS.  These include the thermal management system, the environmental control system, the power and electrical system, and the data acquisition and storage system.  The performance requirements are compiled in Table 6.

The MicroMAPS interface guide stipulates that MicroMAPS be kept within a specific internal temperature range of –5˚ C to 30˚ C to properly process incoming data.  Based on the expected mission profile of Proteus, the vehicle may encounter a temperature range of –57˚ C to 50˚ C during its total mission in the atmosphere.  Designs that are able to monitor and regulate the internal temperature range most efficiently will be valued accordingly.

A proper operating environment is necessary for MicroMAPS to function correctly and minimize data corruption.  In addition to the above temperature requirements, other essential environmental properties of the MicroMAPS system include pressure and humidity regulation.  MicroMAPS requires a clean optical system in order to function properly and minimize data corruption.

Another requirement is to supply power to all MicroMAPS instrument and interface subsystems.  The instrument requires a 24-Watt power supply capable of +5 and ±15 output voltages, and ideally, a backup power system could be included for redundancy.  A power management system is also required to control the power distribution and to ensure that the interference between other systems onboard the Proteus is kept to a minimum.

Before any incoming signals are processed there must be a data storage system in place to compile the information obtained during flight, complemented by a backup storage system.  The instrument is able to gather a maximum of 0.432 MB of data per day, which will be extracted following each mission.

Table 6: Proteus Performance Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| Power and Electrical: | Maximize power and voltage to instrument and subsystems | Watts, Volts |
|  | Maximize power reliability | Watts, Volts |
|  | Minimize interference from multiple systems | Frequencies |
|  | Maximize data reliability | Backup power, Watts |
| Data Acquisition and Storage: | Meet storage requirement | MB per day max |
|  | Maximize data reliability | Data block size in bytes |
|  |  | RAM and ROM |
| Thermal Management: | Meet temperature requirements | Minimize maximum temperature and maximize minimum temperature |
|  | Maximize system thermal isolation |  |
| Environmental: | Minimize contamination | Pressure, humidity, contaminants |

### 2.1.2 Minimization of Cost

To minimize the cost of operating MicroMAPS, four categories must be considered.  These include material cost, power consumption, development and construction cost, and maintenance cost.  These categories apply to all of the operation platforms but are presented here in the context of the Proteus-based operation.  Material cost is a variable dependant upon the nature of materials required to meet mission requirements.  Incorporating common aerospace materials, such as aluminum, eliminates the need to deal with the high cost associated with specialization.  Minimizing energy consumption allows for the use of optimized power system components.  Making use of as many off the shelf components as possible minimizes the need for development and testing funds.  Funding required throughout the maintenance portion of the system life cycle can be diminished through proper pre-production modeling.  The result is an optimal investment of system resources, translating into a cost-optimized system that matches the intended life span.  This information is included in Table 7.

Table 7: Proteus Cost Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| Thermal Management: | Minimize thermal system costs | Cost |
| Power and Electrical: | Minimized power losses | Watts |
|  | Minimize R&D cost | Cost |
| Data Acquisition and Storage: | Minimize subsystems power consumption | Watts |
|  | Minimize R&D cost | Cost |
| Environmental: | Minimize cleaning costs | Cost |

## 2.2 Dedicated Aircraft Objectives

The operation of the MicroMAPS instrument on the dedicated aircraft faces similar performance and cost objectives as in the Proteus case.  A significant factor in the design of the aircraft is the addition of objectives based on the design of the vehicle itself.  Following are the performance and cost objectives used to measure the effectiveness of the dedicated aircraft design.

### 2.2.1 Maximization of Performance

The following subsystems must be optimized for maximum performance of an aircraft dedicated to the operation of MicroMAPS: propulsion, aerodynamics, structures, stability and control, and instrument operations (same as the Proteus platform).  The individual objectives are tabulated below in Table 8.

First, to obtain useful data, the aircraft must have an appropriate propulsion system.  The propulsion system must operate with minimum vibration during flight, as determined through analysis and testing of the frequency and amplitude of oscillation.  In addition, the system must be able to power all of the other systems on the aircraft, including temperature regulation systems and flight systems.  Depending on mission requirements, the aircraft may operate in either long endurance or long range conditions.  The propulsion system must be designed to function at the high altitudes necessary for these conditions.

The aerodynamic properties of the aircraft design are also important.  For the MicroMAPS instrument, the aircraft must be optimized for either long range or long endurance flight.  These conditions require a configuration for extremely high altitudes (measured through the values for CL, CD, and Ccruise), and the design of aerodynamic surfaces must minimize vibration incurred during flight.

Structural loading is another important issue in aircraft design.  The dedicated aircraft must be optimized for stiffness and strength to maintain structural stability during flight and on the ground, while also minimizing the total aircraft weight.  Furthermore, the structure must allow the optimal positioning of the payload, requiring a maximum amount of flexibility in the volume dedicated to the payload.

Throughout flight the aircraft will most likely be subjected to adverse conditions.  A maximum amount of payload flexibility and a minimum amount of trim drag (at high altitude cruise conditions) is therefore required to maintain stability and control.  The MicroMAPS instrument must accurately monitor its target; therefore the aircraft must incorporate an attitude knowledge and control system to allow the instrument to meet the necessary pointing requirements.

In addition to these requirements, the dedicated aircraft must meet certain temperature, power, and data storage requirements as dictated by the MicroMAPS instrument.  These constraints are described in detail in Section 1.3.

Table 8: Dedicated Aircraft Performance Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| Aerodynamics: | Optimize for long range/endurance | (L/D)max (E) |
|  |  | (D/V) (R) |
|  | Optimize for high altitude | CL, CD, Vcruise |
|  | Minimize vibration | Frequency and amplitude |
| Stability and | Maximize payload flexibility | Static margin |
| Control: | Minimize trim drag (high altitude) | CM at high altitude |
| Structures: | Optimize strength | Material/configuration yield strength |
|  | Minimize weight (high altitude) | Material density and volume |
|  | Maximize payload flexibility | Available payload volume |
|  | Optimize stiffness | Material/configuration Young's Modulus |
| Propulsion: | Minimize vibration | Frequency and amplitude |
|  | Maximize power for instrument & subsystems | Watts |
|  | Optimize for high altitude | (L/D)max, Wmin ( T=(D/L)*W |
|  | Optimize for long range/endurance | Distance/vol. of fuel or time/vol. of fuel |

### 2.2.2 Minimization of Cost

There are certain issues to consider when trying to minimize the cost of the dedicated aircraft.  Certainly all of the ways to minimize the cost associated with the instrument operation as mentioned in the Proteus section of this chapter are applicable here as well.  Specific aircraft design choices rely on adherence to the NASA mission goals and most notably require a long range and high endurance aircraft.  Aircraft parameters that affect operating cost include trim drag, fuel efficiency, and flight optimization for high altitudes.  This information is included in Table 9.

Table 9: Dedicated Aircraft Cost Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| Aerodynamics: | Minimize R&D cost | Cost |
|  | Minimize production cost | Cost |
|  | Optimize efficiency at high altitude | Fuel cost |
| Stability and | Minimize trim drag | CD at high altitude cruise, fuel cost |
| Control: | Maximize reliability | Operation hours vs. maintenance hours |
|  | Minimize number of parts | Cost |
|  | Minimize R&D cost | Cost |
| Structures: | Minimize material, construction, maintenance | Cost |
| Propulsion: | Maximize fuel efficiency at high altitude | TFSC |
|  | Optimize for long range/endurance | Fuel cost per unit distance and time |
|  | Minimize R&D cost | Cost |
|  | Maximize reliability | Maintenance cost |

## 2.3 Dedicated Spacecraft Objectives

The dedicated spacecraft platform includes performance and cost objectives similar to the previous cases.  This option is expected to provide the highest performance as well as the highest cost of the three platforms.  The goals for maximization of performance and the minimization of cost for the spacecraft are explained below.

### 2.3.1 Maximization of Performance

The following subsystems must be optimized for maximum performance of a spacecraft dedicated to the operation of MicroMAPS: propulsion, structures, attitude dynamics and control, launch vehicle, and instrument operations (same as the Proteus platform).  The performance objectives of the dedicated spacecraft are compiled in Table 10.

One of the primary advantages of the dedicated spacecraft in the application of MicroMAPS is the ability to monitor a relatively large area for a long period of time.  Depending on the scientific goals, it may be necessary to include a propulsion system capable of efficiently changing or modifying the orbit of the spacecraft.

The MicroMAPS instrument operates at an ideal state under “clean” conditions.  A space mission is not exposed to the same atmospheric conditions as Proteus or the dedicated spacecraft.  Therefore the environment under which MicroMAPS is to be integrated into the spacecraft must be clean to minimize contaminants within the instrument itself.  Such contaminants compromise the quality of the data obtained during missions.

The spacecraft will be exposed to temperature ranges exceeding those for which MicroMAPS is designed.  Therefore, a thermal management system must be in place to measure and regulate the temperature of the instrument.  The system must also monitor the heat produced by auxiliary systems and thermal radiation from the operating environment.

The MicroMAPS instrument must be pointed correctly to obtain useful data. The instrument requires that the spacecraft have an attitude determination and control system capable of ensuring that the attitude control of MicroMAPS is within ±2.5˚ and that the attitude knowledge error is no greater than ±0.5˚.

During launch and operation, the MicroMAPS instrument and the spacecraft will be subjected to varying loads.  The structural design must be sufficient to withstand the anticipated loading from the launch vehicle.  The stiffness of the structure must be such that the vibration of the spacecraft is minimized.  A maximum amount of payload flexibility would allow different configurations to be used for a variety of situations.

A launch vehicle is required to place the spacecraft in low earth orbit (LEO).  The launch vehicle must be selected to minimize the forces acting on the spacecraft during launch.  Lower launch loads correlate to a lower total spacecraft mass.

The same temperature and power requirements of the instrument that were mentioned previously in the Proteus section of this chapter, also apply to the spacecraft.  The instrument gathers a maximum of 0.432 MB of data, and the spacecraft must have the capability to transmit the data periodically to a ground station.  The power used by the transmission and storage system must be kept to a minimum.

Table 10: Dedicated Spacecraft Performance Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| Data Comm.: | Maximize transmission capability | Kbps |
|  | Minimize power consumption | Watts |
| ADCS: | Minimize the attitude knowledge error | Nadir degrees |
|  | Minimize error in attitude control requirement | Nadir degrees |
| Propulsion: | Maximize maneuverability | Isp |
| Thermal | Meet temperature requirement | Operation temperature after launch |
| Management: | Maximize thermal insulation | Heat dissipation of subsystems |
| Structure: | Meet strength requirements | Launch vehicle data |
|  | Provide maximum payload flexibility | Launch faring dimensions |
|  | Optimize stiffness | Frequency and amplitude |

### 2.3.2 Minimization of Cost

There are certain issues to consider when trying to minimize the cost of the dedicated spacecraft.  In addition to the costs associated with the instrument, which have been mentioned previously, unique spacecraft expenses include the necessity for a launch vehicle and the need to use space qualified materials and structures.  Launch vehicle selection will be driven by cost and orbit requirements.  The development of a satellite to meet the mission requirements is limited to pre-approved materials and components.  Use of these materials is a major factor in increasing the cost of the spacecraft option.  This information is included in Table 11.

Table 11: Dedicated Spacecraft Cost Objectives

| Subsystem | Objective | Measure of Effectiveness |
| --- | --- | --- |
| ADCS: | Minimize R & D cost | Cost |
|  | Minimize weight of ADCS system | Launch cost |
| Propulsion: | Minimize fuel use | v |
|  | Minimize cost during production | Cost |
|  | Minimize weight | Launch cost |
| Thermal Management: | Minimize thermal system cost | Cost |
| Structure: | Optimize use of material | Cost |

## 2.4 Summary

This value system design includes the two major objectives of maximizing performance and minimizing cost.  All of the sub-objectives that fall under these two categories are listed by platform and subsystem, along with the appropriate measures of effectiveness. This information is used to compare the options generated during the system synthesis process.  This process uses the value system described in this chapter as a means of arriving at an optimized configuration.

## Chapter 3: Proteus

## 3.1 Mission Overview

The Proteus research aircraft was designed and built by Scaled Composites, Incorporated.  The aircraft is designed to be modular to allow for different configurations depending on payload and mission requirements.  Multiple payloads and missions can be flown and operated on the aircraft during a single flight.  Scaled Composites operates the aircraft in association with the payload designers and operators.  The aircraft is setup to provide multiple mounting points for instrumentation depending on the size and mission requirements.  All payloads can be monitored by the pilots from inside the cockpit for real time data verification and analysis.  The Proteus is optimized for high altitude and long endurance research and thus the payloads are also generally optimized for a flight altitude of greater than 60,000 feet and flights lasting up to 14 hours.49

There are four major components to consider when integrating the MicroMAPS instrument into Proteus:  structural configuration, environmental control, data acquisition, and system power.  The following sections describe in detail the recommended configuration for incorporating MicroMAPS into Proteus.

The Proteus project has been developed with the assistance of three additional parties.  NASA Langley Research Center proposed the project and assisted in mission development and the MicroMAPS operating procedures.  VSGC assisted in the design of the internal structure and interfaces required to operate the instrument on the Proteus.  Scaled Composites aided in the interface between the aircraft and the instrument suite, along with environmental conditions and operational procedures.  The MicroMAPS team would like to extend special thanks to those actively involved:  Vicki Conners, NASA LaRC; Dr. Reichele, NASA LaRC; John Companion, VSGC; Mike Alsbury, Scaled Composites; Don Oliver, NASA LaRC.

The original plans called for the possibility of one or more students to help build and test the Proteus interface for MicroMAPS.  Current plans call for Raytheon to build the electronics suite, and Scaled Composites to build the structural interfaces.

## 3.2 Power

### 3.2.1 System Overview

The instrumentation suite is designed to support all the necessary functions of the MicroMAPS instrument.  One essential function of this structure is to provide power to the instrument and associated hardware.  Power must be supplied to the MicroMAPS instruments power supply, the data acquisition computer, and the environmental sensors.  This power must also be regulated to ensure efficient operation of the hardware.  All voltages mentioned in this section are direct current (DC) voltages unless otherwise noted.

The Proteus aircraft supplies power to the instrumentation suite by power cables running through the wheel well.  Two generators running off the turbofan engines provide up to 800 amperes total current at 28 volts to the entire aircraft.  The problem with the power output from the Proteus generators is that the voltage can fluctuate by as much as one half volt above or below the nominal 28V.

A system of converters will be used to clean, regulate, and monitor the power being supplied to the instrument suite.  Due to the low power consumption of the entire system, small compact converters can be used to save space, improve efficiency, and meet the requirements necessary to operate the instrument and hardware.

The company selected to provide these compact DC-DC converters is Martek Power, an international company with multiple distributors around the United States and the world.  Martek Power has worked on military, commercial, and industrial applications and ships over 1,500,000 products annually.  All products provided by Martek Power meet the military standards given in Table 12, and certain units may meet additional standards as defined in their respective sections.  These requirements ensure that the units will be able to withstand the environmental conditions they are subjected to as defined in Section 3.4.

Table 12: Military Electrical Standards8

| Specification | Condition | Test Condition |
| --- | --- | --- |
| MIL-STD-704D | Input Transient | Transients up to 50 V for 0.1 second |
| MIL-STD-810E | Vibration | Up to 30gs, each axis for 1 hour |
| MIL-STD-810E | Humidity | 95% humidity, non-condensing for 10 days |
| MIL-STD-810E | Temp/Altitude | 40 hours from -55°C to +71°C |
| MIL-STD-810E | Acceleration | 14gs each axis |
| MIL-STD-810E | Temperature Shock | -55°C to +100°C |
| MIL-STD-901C | High Impact Shock | 5 foot hammer drop |

The first step in providing power to the instrumentation suite is to clean and regulate the power.  This will be performed by a Martek Power NB50S converter.  The details of this unit are given in section 3.2.2.  An Electromagnetic Interference (EMI) filter will remove any noise on the input signal.  This unit is the NBF50 and is a passive input filter for the leads of the NB50S.  Details of this unit are given in section 3.2.5.

After the power has been regulated, the MicroMAPS instrument and the PC104 power supplies are connected in series to provide power to their respective instruments.  The PC104 has an internal power supply which can accept a voltage range of 5-40V input.  The total power consumption of the PC104 should not exceed 3 watts.  A model CB5S DC-DC converter will be used to convert the 28V into 15V with a maximum power consumption of 5 watts.  Details of this unit are given in section 3.2.3.  The MicroMAPS power supply has an input of 28V and outputs of 5V and +/- 15V.  This converter is to be supplied by NASA and further details of the instrument are currently unavailable.  A basic diagram of the size of the MicroMAPS power supply is shown in Figure 2.

An alternative solution for the MicroMAPS instrument power supply is the NB45T triple output DC-DC converter (section 3.2.4) offered by Martek Power.  This unit can provide the necessary power and regulation required to efficiently run the instrument and should be coupled with an additional NBF50 EMI filter.

Figure 2: MicroMAPS power supply chassis10

### 3.2.2 Main Power Converter NB50S41

The NB50S converter will be able to supply an adequate amount of power to the entire instrument suite running at peak load conditions.  This unit can accept a range of 14 to 40 volts input, with a brown out occurring at 12 volts.  This range is wide enough to accommodate the voltage generated by Proteus and also enables the instrumentation suite to be used on any other system within the input range of the unit.  Additional details of the converter are shown in Table 13.  Figure 3 shows a detailed schematic of the NB50S.

There is a heatsink attached to the bottom of the module.  The unit is attached to the main-plate through four 4-40 inserts.  There are different options for the arrangements of the input and output pins.  The ideal choice for this system is option A:  pins out of the side of the unit.  This configuration should be used for all modules requiring this option.

The input leads to this unit should be supplemented with an NBF50 EMI filter (section 3.2.5).  In addition, two fuses should be connected in parallel to the positive lead of the NBF50 EMI filter.  These fuses are slo-blow type MDX or equivalent fuses with a minimum current rating of 5 amps and a voltage rating of at least 125V.  The output connections should also be wired into the positive and negative S pins, as shown in Figure 7.  These pins enable remote sensing of voltage to compensate for voltage loss due to wiring.  This feature is not necessary but must be disabled as described.

Table 13: NB50S Main Converter Details41

| Model Number: NB50SM/28-A |
| --- |
|  | Typical | Max | Units |
| Set Point Accuracy |  | 1 | %Vout |
| Load Regulation | 5 | 0.20% | mV |
| Line Regulation | 5 | 0.20% | mV |
| Ripple P-P (10 MHz) (28V) | 0.20% | 1% | %Vout |
| Mechanical Characteristics |
| Weight | 3.2 | oz. |
|  | 90 | grams |
| Size | 3.0 x 1.5 x 0.38 | inch |
|  | 76.2 x 38.1 x 9.7 | mm |
| Volume | 1.71 | inch3 |
|  | 28 | cm3 |
| Material | Pin | Brass (Solder Plating) |
|  | Baseplate | Aluminum 5052-H32 |
|  | Case | 28 Gauge Steel (cold rolled) |
| Finish |  | Nickel Plating |
| Mounting | Standard | 4-40 inserts provided in baseplate |

Figure 3: NB50S Main Converter Schematic41

### 3.2.3 PC104 Power Supply CB5S8

The PC104 and the environmental sensors are run off of an internal power supply inside the PC104 stack.  For more information on this system refer to Section 3.3.3.  The CB5S will supply a clean and regulated voltage of 15 volts to this power supply.  This module has a maximum power draw of 5 watts.  This is more than sufficient for the current PC104 configuration and the 1-wire environmental monitoring bus.  Details of this instrument are shown in Table 14.  A diagram of the unit is shown in Figure 4.

Table 14: CB5S PC104 Power Supply Details8

| Model Number: CB5SM/15 |
| --- |
|  | Typical | Max | Units |
| Set Point Accuracy | 25 | 50 | mV |
| Load Regulation | 5 | 10 | mV |
| Line Regulation | 5 | 10 | mV |
| Ripple P-P (10 MHz) (2V-24V) | 40 | 100 | mV |
| Mechanical Characteristics |
| Weight | 0.53 | oz. |
|  | 15 | grams |
| Size | 1.0 x 1.0 x 0.38 | inch |
|  | 25.4 x 25.4 x 9.7 | mm |
| Volume | 0.38 | inch3 |
|  | 6.3 | cm3 |
| Material | Pin | Brass (Solder Plating) |
|  | Case | Aluminum 5052-H32 |

Figure 4: CB5S PC104 Power Supply Diagram8

### 3.2.4 Triple Output MicroMAPS Power Supply NB45T41

A viable alternative to the power supply already constructed for the MicroMAPS instrument is the Martek Power NB45T.  This unit provides the necessary power for the MicroMAPS instrument through the worst case loads predicted by the interface control document.  Details of this unit are given in Table 15.  A diagram of the NB45T is shown in Figure 5.  An EMI filter NBF50 should be utilized on the input leads to this device to control any unwanted noise on the input signal.

Table 15: NB45T MicroMAPS Power Supply Details41

| Model Number: NB45TM/5/15/15-A |
| --- |
|  | Typical | Max | Units |
| Set Point Accuracy |  | 1 | % Vout |
| Load Regulation | 5 | 25 | mV |
| Line Regulation | 5 | 10 | mV |
| Ripple P-P (10 MHz) | 50 | 100 | mV |
| Mechanical Characteristics |
| Weight | 5.4 | oz. |
|  | 150 | grams |
| Size | 3.0 x 3.0 x 0.38 | inch |
|  | 76.2 x 76.2 x 9.7 | mm |
| Volume | 3.42 | inch3 |
|  | 56.1 | cm3 |
| Material | Pin | Brass (Solder Plating) |
|  | Baseplate | Aluminum 5052-H32 |
|  | Case | 28 Gauge Steel (cold rolled) |
| Finish |  | Nickel Plating |
| Mounting | Standard | 4-40 inserts provided in baseplate |

Figure 5: NB45T MicroMAPS Power Supply41

### 3.2.5 EMI Filter NBF5041

The NBF50 provides additional MIL-STD-461D compliance.  These standards dictate the amount of noise that the voltage is allowed to contain at a range of frequencies.  The unit is a thermally non-dissipative device.  Less than 1 volt is lost is across the NBF50.  The inputs of the NB50S Main Converter and the NB45T MicroMAPS unit should be supplemented with this device.  No additional external components are necessary to run this device.  Details of the NBF50 are shown in Table 16 and Figure 6.

Table 16: NBF50 EMI Filter Details41

| Model Number: NBF50 |
| --- |
| Input Voltage (maximum) | 50 | V |
| Rated Output Current | 5 | A |
| Isolation (Input/Output to Case) | 500 | V |
| Operating Temperature | -55 +100 | oC |
| Storage Temperature | -55 +125 | oC |
| Insulation Resistance (measured at 50Vdc) | 59 | M Ohms |
| Mechanical Characteristics |
| Weight |  | 1.42 | oz. |
|  |  | 40 | grams |
| Size |  | 1.75 x 1.5 x 0.38 | inch |
|  |  | 44.5 x 38.1 x 9.7 | mm |
| Volume |  | 1 | inch3 |
|  |  | 16.5 | cm3 |
| Material | Pin | Brass (Solder Plating) |
|  | Baseplate | Aluminum 5052-H32 |
|  | Case | 28 Gauge Steel (cold rolled) |
| Finish |  | Nickel Plating |
| Mounting | Standard | 4-40 inserts provided in baseplate |

Figure 6: NBF50 EMI Filter Diagram41

### 3.2.6 Heat Dissipation

The amount of heat that each power supply generates can be calculated by equation 3.1.

(3.1) 41

Table 17 gives details of the power devices and the heat output of the system.  The heat generated by the power supplies is small in comparison to the environment, and will not warm the internal pod environment by more than 3 degrees Celsius.

Table 17: Heat generation

| Power Dissipation: 100% Load |
| --- |
|  | Pout | %Max Load | Efficiency | Efficiency (5% SF) | Pdiss |  |
| NB50S | 50 | 100 | 82 | 77 | 14.94 |  |
| NB45T | 45 | 100 | 81 | 76 | 14.21 |  |
| CB5S | 5 | 100 | 81 | 76 | 1.58 |  |
| NBF50 | thermally non-dissipative device |  | 0 |  |
|  |  |  |  | Total | 30.72 | W |
| Power Dissipation: Maximum Useful Load |
|  | Pout | %Max Load | Efficiency | Efficiency (5% SF) | Pdiss |  |
| NB50S | 28 | 56 | 80 | 75 | 9.33 |  |
| NB45T | 24 | 53 | 76 | 71 | 9.80 |  |
| CB5S | 4 | 80 | 79 | 74 | 1.41 |  |
| NBF50 | thermally non-dissipative device |  | 0 |  |
|  |  |  |  | Total | 20.54 | W |

### 3.2.7 Wires, Connectors, and Line Diagram

The hook up wire chosen for the power system is #20 AWG wire.  This wire type has a resistance of 10.13 mOhm/foot.  The amount of voltage lost across this wire is negligible and can be ignored for all power routes.  Connections to all Martek Power supplies are soldered.  Input to the MicroMAPS power supply provided by NASA is done via a D-sub 50 pin connector.  All hookup wire should have a minimum 2 inch diameter safety loop to allow for any thermal or mechanical movement.

A connection diagram for the complete power suite is shown in Figure 7.  F1 and F2 represent the input fuses as detailed in Section 3.2.2.  The diagram is drawn showing the NB45T triple output power supply and EMI filter.  If the NASA instrument is to be used, then these two devices would be removed and the MicroMAPS power supply would replace them.  No further modification is required.

Figure 7: Power System Connection Diagram

## 3.3 Data Acquisition

The MicroMAPS instrument and environmental monitoring suite export data which needs to be recorded.  In addition, certain flight characteristics will also need to be recorded: velocity, position, altitude, attitude, external environmental conditions, and flight time.  The Proteus aircraft exports this data to any payloads that request it, eliminating the need for subsystems such as GPS.  This data must be coordinated with the MicroMAPS data in real time.  The following section describes the hardware integration of this system.

### 3.3.1 Computer55

The computer form factor chosen is the PC104.  This compact device allows for efficient operation in terms of electrical, mechanical, and digital data acquisition.  The PC104 had been widely adopted in the aviation and space industry.  The PC104 is a reliable data acquisition choice and is stable in a multitude of environments.

### 3.3.2 CPU Board

The CPU board chosen for the MicroMAPS data acquisition and collection system is the MZ104+ ZFx86 board.  Integrated within the board is a dual Intel 82559ER 10/100 BaseT fast Ethernet connector, two 16550-compatible RS232 serial ports with baud rates of up to 115.2 K baud, one IDE channel supporting up to two devices, dual USB 1.1 ports, and one enhanced bidirectional parallel port.  The ports for all of these integrated systems lie on the included utility interface card.  The computer will be equipped with a 64 megabyte dimm of SDRAM which shall be purchased separately.  The chosen operating system was Linux, which shall be run from the Solid State Flash Storage.  Operating at a CPU frequency of 100 MHz with 64 megabytes of SDRAM the CPU board consumes 940 mA.  The mechanical specifications of the board can be viewed below as Figure 8.

Figure 8: MZ104+ Mechanical Specifications55

### 3.3.3 Power Board

The computer power supply utilized is a vehicle grade 50 Watt high efficiency DC-DC converter.  The specific board is the HE104 purchased from Tri-M Systems Engineering.  The HE104 is incorporated into the computer design to both clean up and filter the incoming power to the CPU board, as well as any additional I/O boards added at a later time.  The input DC voltage range is from 6 to 40 volts with output voltages of positive 5 and 12 volts with an option for both negative 5 and 12 volts.  Heavy duty load dump transient suppressors rated for 5000 Watts are utilized to regulate voltage spikes often common in vehicle operations.  Load regulation efficiencies are up to 95%.  The HE104 also incorporates a remote on/off capability that allows the power supply to remain on with steady power as the computer shuts itself down.  After an inputted time the power supply will then power itself down.  Table 18 shows both the electrical and mechanical specifications of the HE104.

Table 18: Electrical and Mechanical specifications of the HE10455

| Characteristic | Value |
| --- | --- |
| 5V output * | 10A |
| 12V output | 2A |
| -5V output | 400mA |
| -12V output | 500mA |
| Input Voltage Regulation | 6 to 40V |
| Load Regulation ** | <60mV |
| Line Regulation ** | 40mV |
| Output temp. drift ** | <40mV |
| Switching Frequency | 75kHz |
| Max. Input Transient | 125V for 100msec |
| Output Ripple ** | <20mV |
| Conducted Susceptibility ** | >57db |
| Efficiency ** | up to 95% |
| Temp. Range | -40 to 85C |
| Quiescent current *** | 2mA |
| Size, PC/104 form factor compliant**** | 3.55"W x 3.75"L x 0.6"H |
| * | Current rating includes current supplied to 12V, -12V, & -5V regulators |
| ** | Measured on the 5V output |
| *** | LEDs disabled, Low Quiescent mode enabled |
| **** | Not including pass-through pins |

### 3.3.4 PC104 Enclosure

The enclosure for the PC104 computer system was chosen as the CT104 from Tri-M Systems Engineering.  The case is constructed from anodized aluminum and sits on top of a rubber anti-shock mounting pad.  The PC104 cards are supported by four corner-mounted rubber guides that secure and isolate the cards from the aluminum chassis.  An enclosure length of 6 inches was chosen to allow for further expansion of either a second PC104 system or additional I/O cards for further data acquisition.  Custom aluminum end caps were chosen that comply with the inputs and outputs of the MZ104+ CPU card.  Physical dimensions of the enclosure can be viewed in Figure 9.

Figure 9: CT104 Enclosure – 6 inch depth55

### 3.3.5 System Setup

The MZ104+ CPU board was chosen to eliminate the need for a separate Input/Output (I/O) board.  The wiring setup for the computer system shall be briefly discussed in the following section.

The enhanced bidirectional 25-pin parallel port on the CPU Utility interface card will connect directly into the MicroMAPS instrument.  This port is located on the front, or optic side of this instrument.  The required length of parallel port wiring, due to the placement of the instrument and the PC104 computer, is well within the parallel port signal degradation limits that would be due to the length of the connecting wire.

One RJ45 Ethernet cord will be run from the computer to the suite base plate where it will be connected to the aircraft Ethernet network through the use of an aircraft grade sealed connector, provided by DigiKey17.  This Ethernet network shall connect the PC104 computer to a laptop computer that will be used to monitor the system status of the instrumentation suite as well as to parallel the data taken.

The second Ethernet connection will go to the same exterior panel as the environmental pump and purge valve using sealed aircraft grade connectors.  This port will be utilized for easy access to the PC104 from the ground for monitoring of internal pressure, humidity, and temperature, or for direct data extraction.  The data will be stored on a compact flash card as a temporary storage solution.  The card will be on the order of 256 to 512 megabytes of memory.

For more long term solutions the PC104 allows the use of IDE hard drives.  The flight profile of the Proteus aircraft, as to be utilized for data gathering for the MicroMAPS instrument, maintains a smooth enough flight as to allow the use of any IDE hard drive for mass storage if necessary.  The G-loads as experienced by the pod are under the failure loads of a normal off the shelf IDE hard drive.  Up to two hard drives can be connected in series through the IDE interface.  One of the RS232 9-pin serial ports shall be used to take the outside data from the networked flight computer to correlate with the instrumentation data.  The two samples of data will be connected through a time stamp.  The second RS232 9-pin serial port shall be connected to the 1-wire bus card and from this card a single RJ11 telephone cord will be placed around the instrument suite that will contain the internal environmental telemetry sensors.  This card and the associated sensors are discussed in more depth in the environmental section.

3.4 Environmental Monitoring System

Through a joint effort by Virginia Tech and Virginia Space Grant Consortium an environmental control system was developed for the safe and successful operation of the MicroMAPS instrument and all other components.  The following internal pod conditions were established for the optimal performance of the MicroMAPS instrument: the internal pod temperature will not be regulated since MicroMAPS performs better in a cold environment, and humidity shall be kept at or near zero percent in order to minimize condensation.

### 3.4.1 1-Wire® Network14

The 1-Wire® net, sometimes referred to as a MicroLAN, is a low cost bus based on a PC or microcontroller communicating digitally over a twisted pair cable with 1-Wire® devices.  The system consists of three main elements: a bus master with controlling software, the wiring and associated connectors, and 1-Wire® devices.  Each device connected on the 1-Wire® net is encoded with a 64-bit serial code unique to each device so that is can be called up by the bus master.  In order to achieve maximum performance, CAT 5 UTP (unshielded twisted pair) cable is recommended for use in routing the 1-Wire® net.  Power is provided to the 1-Wire® net over the same line used for communication and ranges from 3.5 to 5 volts.

It was determined that the internal pod temperature would not be regulated, but monitored using a number of 1-Wire® Digital Thermometers developed by Dallas Semiconductor.  The DS18S20 1-Wire® Digital Thermometer measures temperatures from

-55°C to +125°C (-67°F to +257°F) and has an accuracy of ±0.5°C from -10°C to +85°C14.  Temperatures inside the pod during the entire mission profile will vary from +50°C on the ground to -10°C at cruise altitude making the DS18S20 a perfect choice for temperature observations.

Figure 10: DS18S20 1-Wire® Digital Temperature Sensor14

Humidity and condensation inside the pod will be controlled by a pump and purge system similar to the model currently used with the NAST-I experiment on the Proteus aircraft.  The system will pump UHP (ultra high pure) nitrogen at 5 PSI into the pod resulting in a dry environment with humidity at or near zero percent.  Internal pod humidity will be measured using the HMP-2001S Digital Humidity Sensor developed by Point Six, Incorporated.  The HMP-2001S was designed for use non-condensing environments and is suitable for wall or surface mounting.  It is able to measure humidity levels from 0-100 % and has an accuracy of 5% at 25°C.43  Internal pod pressure will remain at a constant 5 PSI and will be monitored using a BAR-2001S Pressure Sensor also developed by Point Six, Incorporated.  The sensor is calibrated and temperature compensated for accuracy and stability.  Both sensors require an external supply voltage of 5V and have a built-in multidrop controller for CAT-5 twisted pair networking.

Figure 11: HMP-2001S Digital Humidity Sensor (left) and

BAR-2001S Pressure Sensor (right)43

### 3.4.2 1-Wire® Serial Interface35

The TEMP05, developed by Midon Design, was selected to be a serial logging interface between the 1-Wire® net and the host PC104.  It was setup to log and read up to 60 1-Wire® devices ranging from 1-Wire® Digital Thermometers to 1-Wire® Pressure Sensors.  The TEMP05 can be configured to send readings from sensors through the serial port every 1 to 99 minutes and can be adjusted in 1-minute increments.  The TEMP05 comes fully assembled and equipped with V5 software in order to control devices over the 1-Wire® net.  The TEMP05 is to be placed in the PC104 stack.

Figure 12: TEMP05 1-Wire® Serial Interface35

### 3.4.3 Thermal Compound

ECCOBOND 57C, developed by Emerson and Cuming, was chosen as the thermal compound to be used in the instrument suite because of the low outgassing and high thermal conductivity properties.  ECCOBOND 57C is a two component, silver filled, epoxy adhesive.  It has a thermal conductivity of 7.2 W/(mK), a temperature range of –40 to 90°C, and an outgassing value of 0.04.  This epoxy will be applied to any component of the instrument suite that makes direct contact with the thermal mass to allow heat to dissipate from the component to the thermal mass.  The adhesive nature of this product will also aid in keeping the components attached to the thermal mass.

## 3.5 Structure

The structure of the instrument suite is designed to comply with several requirements.  Foremost, the entire complement of instrumentation must be physically stable during operation, and in a position to effectively acquire information from the environment.  Secondly, in order for many of the instruments to maintain optimal performance, an environmental regulation system must be in place.  The tertiary goal for the pod’s structure is that all human interactions with the pod itself (i.e. information gathering, manual environmental regulation, and installation) require minimal expertise and maximum ease in their respective execution.

### 3.5.1 Systems and Weights

In order to ensure that the pod is securely attached to the boom it is first necessary to determine the weights and sizes of the objects inside the pod.  The complete PC104 data acquisition system weighs approximately 10 lb and has been modeled to have the dimensions of 7.1 inches by 6 inches as indicated in Figure 13.  The case for this device is composed largely of aluminum with 4 rubber anchors inside of the shell, one at each corner.  These assist not only in the physical installation of each PC104 card, but they also assist somewhat in vibration control.  The PC104 case mounts on a square rubber base, 6 inches wide, which in turn mounts on to the base platform via 4 3/8-inch screws.

Figure 13: PC104 Exterior Casing and Mounting Base (all dimensions in inches)

The MicroMAPS instrument (Figure 14) weighs at maximum 14 lb.  It has a cylindrical viewing aperture 3 inches long and 1.6 inches in diameter.  The rest of the instrument is 10 inches long, 5 ¾ inches tall and 5 3/8 inches wide.  There are two 25-pin connectors and two 15-pin connectors on the front.  Four feet are attached to the base of MicroMAPS through which 5/16-inch holes are drilled.  Through these holes screws will pass to anchor MicroMAPS to the base platform.

Figure 14: MicroMAPS Diagram (inches)

There are several items which comprise the power regulation and supply system.  These are discussed in detail in section 3.2 of this document.  Figure 15 shows the NBF50 EMI filter, Figure 16 shows the CB5S PC104 power supply, and Figure 17 shows the NB50S main converter.  Figure 18 shows the power supply, which is to be used exclusively with MicroMAPS.

Figure 15: NBF50 Diagram (inches)

Figure 16: CB5S Diagram (inches)

Figure 17: NB50S Diagram (inches)

Figure 18: MicroMAPS Power Supply Diagram (inches)

The nosecone, shown in Figure 19, is constructed from fiberglass and weighs approximately 10 lb.   The nosecone serves to both enable the aircraft to maintain normal flight operations due to its shape, which is built to model the existing pods of the Proteus aircraft.  To seal the pod, a collar is attached to the inside of the nosecone, near its base.  The collar had 8 ½-inch bolts imbedded within it to attach to the base platform and the gasket.

On the lower inboard side of the pod, a panel opens to reveal three input/output ports.  These ports, manufactured by DigiKey17, are sealed connectors to the inside of the pod.  One port is reserved for the immediate access to the Ethernet cable.  The other two ports exist to facilitate pump and purge operations once the pod is sealed.

### 3.5.2 MicroMAPS Viewing Window

On the side of the pod facing the ground there is a hole cut out with a diameter of 2 inches.  This is to accommodate the viewing window through which MicroMAPS must receive data. The window is made from IRTRAN-4, a material supplied by NASA specifically for MicroMAPS.  Its properties complement the IR spectrum required for the device to work properly.

Figure 19: External Pod Diagram

### 3.5.3 Instrument Suite Mounting Platform

The aluminum base platform (Figure 20) weighs slightly more than 63 lb.  It is constructed out of 6061-T6 aluminum alloy primarily due to its relatively good corrosion resistance.  Eight holes situated along the outer flange bolt to the nosecone through a gasket to maintain a hermetic seal for the instrument suite.  Ample room is provided on the main face to allow future additions.  The most likely addition would be in the form of an elevated shelf, which can be screwed to the platform.  This would allow almost limitless potential for future payloads.

Figure 20: Base Platform Diagram, 6061-T6 Aluminum (inches)

In order to account for the weights of the fasteners and the main gasket, the total payload weight is approximated as 100 lb.

The nacelle skin extends 10 inches from the bulkhead where the payload is attached to it with half-inch bolts to the nacelle wall.  According to Scaled Composites, this method of attachment is capable of supporting up to 140 lb.  A separate flange on the inside of the nosecone bolts to the base platform.  The instrument suite is then hermetically sealed by way of the gasket between the nosecone flange and the base platform.  This is shown in Figure 21 where the base platform is colored gray and other parts are indicated accordingly.

Figure 21: Pod Mounting Configuration10

To permit the instrument suite (in particular, MicroMAPS) from collecting poor data, the entire pod must be isolated from the external environment.  As briefly discussed above, Figure 21 illustrates the installation scheme in which the nosecone structure and the base platform form a seal with a rubber gasket at their interface.  The connections to the base platform and through the nosecone are sealed to prevent the isolated environments from leaking in or out.  The pump and purge valves located on the inboard side of the nosecone (Figure 19) pressurize the pod with ultra pure nitrogen gas to remove any appreciable amount of water in the pod.

### 3.5.4 Installation and Configuration

The third main consideration in designing the payload installation is to ensure that all interactions with the pod are easily carried out.  The pod has a set of internal connections to the Proteus aircraft: one RS-232 interface to relay flight data to the PC104, one Ethernet jack to relay information from the PC104 to the on-board laptop computer, and the parasite power supply from Proteus to power the instruments.

After the physical installation of the pod, there are two sets of external connections which must be used.  The first set, used prior to takeoff, is the set of pump and purge valves which infuses the internal environment with Nitrogen gas.  The second connection through the nosecone is another Ethernet jack, which allows data that the PC104 has compiled to be accessed either directly on the runway or after the payload has been physically removed from the aircraft.  The installation scheme for the pod is quite simple.  The suggested method of installation is as follows:

- All of the internal connections between the PC104, the MicroMAPS device, the 1-wire bus, and the power supplies must be made (this is discussed in detail in sections 3.2, 3.3, and 3.4).

- On the instrument-side of the base platform, cables are to be run from the DigiKey sealed connectors to their respective instruments.  The RS-232 and the Ethernet cable run to the PC104 computer, the power cable runs to the NB50S main power supply.  One additional internal Ethernet cable must be run from the PC104 to the jack on the inboard interior of the nosecone.  This permits data to be downloaded directly on the runway without removing the entire nosecone.

- After all of the internal connections are properly secured, the nosecone may then be attached.  A gasket is placed on the flange of the base platform, and then is compressed by the nosecone, which slides over the top of the platform.  The protruding bolts in the nosecone should slide through the holes in the gasket and through the holes in the base platform such that the viewing window coincides with the field of vision of the MicroMAPS instrument.  On the other side of the base platform flange, the bolts are then tightly secured with the appropriate nuts and washers.

- The instrument suite is now sealed.  The inboard panel of the nosecone should then be opened to reveal the Ethernet jack and the pump and purge valves (all sealed connectors by DigiKey connectors).  Utilizing the pump and purge valves, the pod must be filled with ultra high pure nitrogen gas to 5 pounds per square inch above atmospheric pressure.  Extra care should be taken to ensure that the seal remains intact so that no nitrogen gas escapes the sealed connections, the viewing window, or the aft end of the nosecone.

- The outputs from the Proteus vehicle are now connected to the jacks on the aft side of the base platform.  The RS-232, input power, and Ethernet cables are to be connected to the three DigiKey sealed connectors shown in Figure 20.

- Finally, the pod is placed inside the nacelle.  The inside of the nosecone slides over the slightly smaller nacelle lip and is bolted in place with 8 countersunk screws of ½-inch diameter around the nosecone.  This way the entire nosecone may be detached while the interior environment of the instrument suite remains undisturbed.

Chapter 4: Menelaus

## 4.1 Introduction

In this chapter, the aircraft design is taken from RFP requirements to final proposal.  The chapter is organized as follows: Request for Proposal (RFP), Selection of the Final Design Concept; Detailed Sizing; Propulsion; Aerodynamics; Stability and Control; Performance; Materials and Structure; Systems; Cost; and Final Proposal.

## 4.2 Aircraft RFP

The need for an aircraft to carry out atmospheric observation with MicroMAPS evolved over the last three decades.  In the 1970s, scientists developing chemical and transport models for atmospheric gases identified a need for a “long term measurement program for atmospheric CO, CH4, and OH concentrations” in the troposphere.53  In response, large and rather crude space-based instruments, like MAPS (Measurement of Atmospheric Pollution for Satellites), were developed and deployed.  NASA’s small satellite technology initiative (SSTI) then instigated the development of a second-generation instrument.  The motivation for the new design was to make the instrument smaller, cheaper, and more useful.  The result is MicroMAPS.

MicroMAPS was originally designed as a space-based platform, but the scientists at NASA Langley Research Center (LaRC) realized that operating the instrument onboard an aircraft could offer excellent data gathering opportunities.  The aircraft platform affords several advantages over the satellite platform.  These advantages include lower cost, more detailed local data, improved geophysical data, and the capacity to respond to and track specific emissions episodes, amass detailed column distribution data, and fly in multi-aircraft, multi-instrument coordinated missions.

The cost of launching a satellite of this size into low earth orbit (LEO) is on the order of ten to twenty million dollars.  For a fraction of that cost, MicroMAPS could be operated in atmospheric flight, taking advantage of the flexible mission profile an aircraft platform offers.

Aircraft-based operation of MicroMAPS allows gathering of ultra-fine and spatially varying data.12  A spacecraft in LEO has a ground speed of about 15,000 kts (~17,000 mph) and cannot change its direction.  The observational opportunities are limited to a fast-moving, fixed-swath-width, linear path that requires many orbits to pass over the same location on earth twice.  Onboard an aircraft, the instrument can gather much finer data due to the relatively slow ground speed.  The ground track is not limited to one direction, but is determined at the scientists’ discretion.

MicroMAPS can gather better geophysical data from the relatively low operational altitude onboard an aircraft than it can from LEO.12  The instrument uses earth-generated infrared radiation (IR) to detect the absorption line spectra of trace gases in the atmosphere.  This radiation, like all electromagnetic radiation, decreases in strength in proportion to the square of the distance from its source.  The IR signal at high altitude, atmospheric flight (~65,000 ft) will be about 350 times stronger than that available at LEO altitudes.

An aircraft-based instrument allows scientists to respond to specific emissions episodes and to track their effect on atmospheric chemistry.12  These events include natural sources of gases, such as a volcanic eruption, and anthropogenic sources, such as biomass burning caused by deforestation.  A spacecraft, constrained by its orbit, cannot respond to specific episodes.

With its capacity to operate the instrument at various altitudes, an aircraft platform allows MicroMAPS to gather extensive altitude profiling data.12  Column distribution measurements can be made from LEO, but the detail of the data is limited by the spacecraft’s fixed altitude.  An aircraft can fly any altitude schedule the scientists wish, giving them more options for data gathering.

An aircraft-based instrument could be operated in multi-aircraft coordinated missions.  These coordinated flights could provide multi-platform validation, enhanced measurement from combined instruments, a wider effective swath, and a larger coverage zone.12  Each aircraft could be fitted with a MicroMAPS instrument or with a different instrument.  This type of coordinated data gathering offers the scientists a great deal of flexibility with their science goals.

An aircraft platform is desirable for the mission flexibility and unique data gathering opportunities it affords the scientists.  To maximize these benefits, the requirements of the RFP have been developed.  They are stated and explained below.

- The cruise altitude shall be no less than 60,000 ft [65,000]*.  This altitude will place the instrument far enough above the troposphere (0 to 36,000 ft) and will give a wide enough viewing swath to gather the desired data.

- The maximum endurance at cruise altitude shall be no less than 36 [40] hours without refueling.  This endurance will allow tracking of specific emissions episodes and will allow extended mapping missions.  The endurance mission profile is shown in Figure 22.

- The maximum range shall be no less than 7,000 NM [8,000].  This range will allow extended tracking and mapping missions.

- The cruise velocity in the maximum range configuration shall be no less than 250 ktas [200 ktas] and in the maximum endurance configuration shall be no less than 250 ktas [150 ktas].  These velocities are consistent with the tracking and mapping missions.

- [The aircraft shall be capable of efficient flight in a range of flight conditions, including low altitude flight and continuously climbing and descending flight.  This capability will allow extensive altitude profiling missions.]

- The payload bay shall be modular.

- The minimum payload capacity shall be no less than 250 lb.

- The payload vibrations shall be kept to a minimum.

- The life-cycle maintenance cost shall be kept to a minimum.

Figure 22: Endurance Mission Profile

## 4.3 Selection of Final Design Concept

In this section, the two final initial design concepts are presented and compared.  One concept is chosen based on its responsiveness to the RFP requirements, feasibility, and cost, among other criteria.  The chosen design is then critiqued, and suggestions for further improvement are proposed.  In subsequent sections, these suggestions, where the analysis show they are appropriate, are incorporated into the design.

### 4.3.1 Menelaus I

Menelaus I is designed to be a highly efficient, long-range, long-endurance research platform, as required by the RFP.  Its lightweight, composite construction and large wingspan allow it to reach the design cruising altitude of 65,000 ft (Figure 23).  The aircraft’s compact size minimizes profile drag and cost.  A modular payload bay is situated in the forward end of the fuselage.  The aircraft’s a single turbofan engine, embedded in the fuselage to minimize drag, will provide enough power for high altitude flight.  The tail control surfaces are contained within a V-tail.

Figure 23: Menelaus I

### 4.3.2 Menelaus II

Menelaus II is laid out with a high aspect ratio main wing and two pitch control surfaces, one forward of the main wing, the other aft (Figure 24).  The wing layout allows efficient high altitude flight (65,000 ft), ample fuel storage (long range/long endurance), and the capacity for efficient flight at range of static margins (modular payload bay).  Two fuel booms extend from the foreplanes to twin vertical tails, furthering the aircraft’s fuel capacity.  The axi-symmetric fuselage nosecone is free to rotate around its axis, allowing a control system to maintain nadir pointing during a turn.  A small turbofan engine drives the aircraft.  The air intake is on top of the fuselage, well aft.  This system offers excellent efficiency at high altitude and meets the cruise speed requirement (250 ktas).  If later trade studies show a turboprop or a piston motor-driven propeller to be more appropriate, this concept could be modified to accommodate the change easily.

Figure 24: Menelaus II

### 4.3.3 The Decision and Suggested Changes

The decision matrix in Table 19 is used to decide between the two concepts.  The criteria for this decision are developed directly from the RFP and from a general consideration of feasibility.  Each design is then given a numerical rating with respect to each category.  The numerical scale ranges from –2 to 2, where –2 is the least desirable, 2 is the most desirable, and 0 is neutral.  The numerical values are multiplied by the scaling factor and averaged.  The design with the highest score is selected for further development.  Menelaus II, with a score of 24, is selected as the final concept.

Table 19: The Decision Matrix

| Category | Scaling | Menelaus I | Menelaus II |
| --- | --- | --- | --- |
| Existing designs | x2 | 2 | 1 |
| TOGW | x4 | 1 | 0 |
| Endurance/Range | x5 | 0 | 1 |
| Altitude | x5 | 0 | 0 |
| Instrument operations | x5 | 1 | 2 |
| Modularity | x4 | 1 | 2 |
| Marketability | x3 | 0 | 1 |
| Innovation | x1 | -1 | 1 |
| Total cost | x5 | 1 | -1 |
| Totals |  | 21 | 24 |

Before moving forward with final sizing and analysis, a critical examination of the final concept reveals the following shortcomings.  The design is too big for the size of the payload, particularly in its length.  A shorter, more compact design would lighten the aircraft and allow the main wing to be positioned closer to the center of gravity.  If the fuel, the only consumable during flight, were placed mostly in the wings, the change in center of gravity would be small over the course of a mission.  This characteristic would eliminate the need for three pitch control surfaces, resulting in a simpler, lighter aircraft.  The booms, no longer necessary for fuel storage, are still conveniently placed to hold the landing gear.  In lieu of carrying fuel, the booms can hold the flight control system, avionics, radar, and other systems, freeing space in the fuselage for the payload, fuel system, engine, and additional fuel tanks.

The empennage design, with two vertical surfaces and a connecting horizontal surface looks over-sized and heavy.  It could be redesigned as an inverted V-tail (this tail configuration will be referred to as an A-tail for the remainder of the report).  This configuration could reduce drag by decreasing the wetted surface area and could save structural weight.

These suggested changes are evaluated and implemented in the following sections.

## 4.4 Detailed Sizing

Before the final round of sizing is performed, the suggested changes to the design are incorporated.  The aircraft’s fuselage and tail booms are shortened.  The booms’ noses are placed just forward of the main wing, and the foreplanes are eliminated.  The empennage design is changed from two vertical surfaces and a joining horizontal surface to an A-tail, which incorporates pitch-yaw control surfaces (these surfaces will be referred to a ruddervators for the remainder of the report).  The design is shown in Figure 25.

Figure 25: New Configuration, Including Changes Developed in Decision Process

The resulting concept is a low wing monoplane with axi-symmetric fuselage and tail booms.  The A-tail supports the ruddervators and, at its apex, a satellite communications dome.  The fuel is stored primarily in the high aspect ratio wing, which is mounted near the aircraft’s center of gravity.  The tail boom noses, which extend forward of the main wing’s leading edge, house a collision control system that will sense other aircraft and execute tactics to avoid them autonomously.  (Such a system is under development at NASA and has been successfully tested onboard Proteus.) 39  The analysis that justifies this configuration is developed in sections dedicated to the aircraft’s subsystems.

### 4.4.1 Sizing Process

Detailed sizing is accomplished using two methods.  First, a detailed analysis of data gathered from existing aircraft that meet some of the RFP requirements is performed.  A weighted average of the value of interest is calculated, giving more weight to those aircraft that more closely match the RFP aircraft.  In some cases, only this empirical method is used.  Second, a number of aircraft design sizing algorithms are used.45  The results of both these approaches are combined to create a reasonable estimate for the aircraft’s characteristics.  The estimations are presented in tabular form with explanations where appropriate.

The estimation of the coefficient of lift (CL) at cruise is developed from existing aircraft in Table 20.

Table 20: Estimation of CL

| Aircraft | Weighting | CL |
| --- | --- | --- |
| Predator B | 1.0 | 1.0 |
| Altair | 1.5 | 2.0 |
| Altus | 1.5 | 1.0 |
| Perseus B | 2.0 | 0.7 |
|  | Average | 1.1 |

The estimation of the wing loading (W/S) and span loading (W/b) is developed from existing aircraft in Table 21.

Table 21: Wing Loading and Span Loading

| Aircraft | Weighting | W/S (lb/ft2) | Weighting | W/b (lb/ft) |
| --- | --- | --- | --- | --- |
| Predator B | 2 | 27.3 | 1 | 100.0 |
| Altair | 2 | 22.2 | 1 | 81.4 |
| Altus | 3 | 16.3 | 2 | 38.5 |
| Perseus B | 3 | 11.3 | 2 | 30.8 |
|  | Average | 18.2 | Average | 53.3 |

The takeoff gross weights (TOGWs) for a turbofan propulsion system and a turboprop propulsion system are developed using a design algorithm in which specific fuel consumptions for different engines and the aircraft’s general dimensions are input, and the aircraft’s TOGW is returned.45  The assumptions, inputs, and results are shown Table 22.

Table 22: TOGW for Turbofan and Turboprop

| Assumptions |  |  |
| --- | --- | --- |
| Propeller Efficiency | 0.85 |  |
| L/D | 30 |  |
| SFC (thrust) | 0.5 | 1/hr @ Cruise |
|  | 0.4 | 1/hr @ Loiter |
| We/W0 | 0.4 | existing aircraft |
| Results | TOGW (lb) | TOGW (lb) |
| Turboprop | 1950 | 3179 |
| Turbofan | 2599 | 1901 |

The results suggest that a turbofan would result in a lighter aircraft.  Although counterintuitive, the result is bolstered by the design trends in high altitude UAV design.  General Atomics plans to replace its successful, turboprop aircraft Predator B with a turbofan powered derivative called Altair.

The TOGW estimate is further refined in Table 23, which presents a weighted average of existing aircraft.

Table 23: TOGW Estimated from Existing Aircraft

| Aircraft | Weighting | TOGW (lb) |
| --- | --- | --- |
| Predator B | 1 | 6400 |
| Altair | 1 | 7000 |
| Altus | 1.5 | 2130 |
| Perseus | 1.5 | 2200 |
|  | Average | 3979 |

The combined results from the Table 22 and Table 23 result in a TOGW estimate of 3000 lb.  The wing area is estimated using the definition of wing loading, i.e. weight divided by wing area, and the estimated TOGW.  The estimated wing area is 164.8 ft2.

The aspect ratio (AR) is estimated from existing aircraft data in Table 24.

Table 24: Aspect Ratio Estimation

| Aircraft | Weighting | AR |
| --- | --- | --- |
| Predator B | 1.0 | 17.5 |
| Altus | 3.0 (longest range) | 23.5 |
| Altair | 1.0 | 23.3 |
| Perseus B | 1.0 | 26.4 |
| Global Hawk | 3.0 (longest endurance) | 25.0 |
| Proteus | 1 | 19.7 |
|  | Average | 23.25 |

The span is estimated from the definition of aspect ratio, i.e. AR = b2/S, to be 58.75 ft.

The ratio of thrust to weight (T/W) is estimated from existing aircraft data in Table 25.

Table 25: Thrust-to-Weight Ratio

| Aircraft | Weighting | T/W |
| --- | --- | --- |
| Predator B | 3.0 | 0.438 |
| Altair | 1.0 | 0.329 |
| Global Hawk | 1.0 | 0.277 |
| Proteus | 1.0 | 0.368 |
|  | Average | 3.80 |

The thrust is calculated from the definition of the trust-to-weight ratio.  The estimation of sea level thrust is 1,141 lb.

A constraints diagram is constructed to further refine the estimation of thrust-to-weight ratio and wing loading.  This diagram is presented in Figure 26.

Figure 26: Constraints Diagram to Optimize T/W and W/S

The constraints mapped on the plot are all developed from standard aircraft performance equations and include the following: climb gradient, landing field length, cruise conditions, and takeoff field length.33  Clearly the climb gradient is the dominant constraint.  By meeting that requirement, the aircraft far exceeds the cruise and takeoff field length requirements.  The design position for the aircraft is to achieve a thrust-to-weight ratio of 0.4 and a wing loading of 18.2 lb/ft2.  These goals place the design in the feasible region of the plot.

### 4.4.2 Sizing Results

The results of the sizing process are tabulated in Table 26.

Table 26: Results of Aircraft Sizing Process

| Parameter | Value | Units |
| --- | --- | --- |
| CL @ Cruise | 1.1 |  |
| W/S | 18.2 | lb/ft2 |
| W/b | 53.3 | lb/ft |
| TOGW | 3000 | lb |
| S | 164.8 | ft2 |
| AR | 23.25 |  |
| b | 58.77 | ft |
| T/W | 0.38 |  |
| TSL | 1141 | lb |

## 4.5 Propulsion

The Menelaus power plant is discussed in this section.  First, the requirements that drive the engine selection are detailed and quantified.  Then, an outline of alternative engines is presented.  The field of alternatives is narrowed to the optimal solution.  The chosen system is then incorporated into the aircraft fuselage, and its operation and maintenance is discussed.

### 4.5.1 System Requirements

The engine must be optimized for the aircraft’s small size and take off gross weight—27 ft and 3000 lb, respectively.  The RFP requirement of a maximum time to climb to 60,000 ft of 90 minutes is a significant constraint on power plant selection.  To meet this requirement, the aircraft must produce a large amount of thrust at sea level.  Since the aircraft is overpowered at sea level, the take off field RFP requirement, traditional a strong factor in engine selection, is not a driving factor.  The remaining requirements, as illustrated in the constraints diagram (Figure 26), are to achieve a thrust-to-weight ratio of 0.4 and a wing loading of 18.2 lb/ft2.  These performance baselines indicate that the class of engines to be considered is in the 1,000- to 2,000-lb thrust class.

Maintaining cruise at 60,000 ft is the most demanding condition the engine will experience.  The required power plant must provide the necessary thrust to maintain Mach 0.44 at the cruise altitude.

### 4.5.2 Engine Selection

To limit development costs, it is necessary for Menelaus to be powered by a commercial off the shelf (COTS) engine.  Only a few existing engines can meet the strenuous RFP requirements, and the search quickly zeroed in on a single family of engines: the Williams/ROLLS FJ series of turbofans.  A comparison table of these power plants is shown below in Table 27.

Table 27: Initial Engine Candidates62

| Model | Type | Thrust @ SL (lb) | SFC (1/hr) | Max Dia. (in) | Max Length (in) | Dry Weight (lb) | Bypass Ratio |
| --- | --- | --- | --- | --- | --- | --- | --- |
| FJ22 | TF | 700 | ~0.486 | 14.5 | 41.0 | 85 | * |
| FJ33 | TF | 1200 | ~0.486 | 19.0 | 37.8 | <300 | * |
| FJ44-1A | TF | 1900 | 0.48 | 20.9 | 46.7 | 452 | 3.3 |
| FJ44-1C | TF | 1500 | 0.48 | 20.9 | 46.7 | 459 | 3.4 |
| FJ44-2C | TF | 2400 | ~0.486 | 47.2 | 21.8 | >500 | * |
| FJ44-3 | TF | 3000 | ~0.486 | 22.96 | 62.32 | >500 | * |

*Data not available

The FJ22 was initially chosen as the best power plant, but the engine, which is still under development, failed to meet performance goals during test runs in 2002.19  In the interest of fielding a more stable system, one that has more flight heritage, the FJ44-1A is chosen.  This engine is both FAA and JAA certified and has been subjected to thousands of accelerated mission test cycles.  The given thrust of 1,900 lb is beyond the Menelaus requirement, and thus the engine will be scaled down to 1,200 lb.  This application of rubber engine sizing is appropriate, as it has been recommended by the Williams Company that the FJ44-1A engine be used for just such a purpose.  The resulting power plant’s specifications are presented in Figure 27 and Figure 28.

Figure 27: FJ44-1A Propulsion System62

Figure 28: FJ44-1A Variant Properties62

### 4.5.3 FJ44 Performance Characteristics

Williams International provided the engine parameters, with further data being interpolated via standard on/off performance algorithms.  Figure 29 outlines the variation in thrust as the engine undergoes variation in altitude and Mach number.  The engine’s specific fuel consumption (SFC) under various conditions is also highlighted.  Although the power plant performs adequately in every respect, the values for SFC are larger than desired.  This is due to the adaptation of this system into a flight profile that is higher in altitude than the engine design conditions.  As conformation of the takeoff and landing performance of the aircraft, Figure 30 shows takeoff thrust rating as affected by various altitudes and ambient temperatures.  This series of data indicates that excess power is provided under all reasonable field conditions.

Figure 29: Net Thrust and SFC for FJ44 Variant

Figure 30: Take-off Thrust under Varying Conditions

### 4.5.4 Engine Ducting

Two engine placement configurations are practical in the Menelaus airframe.  The first is to enclose the engine and avionics in an attached pod above the fuselage, as in the Northrop Grumman Global Hawk aircraft.  This option is the most simplistic and requires minimal alteration to the airframe.  The second is to integrate the engine into the fuselage, requiring ducting to deliver airflow from the inlet to the power plant.  This latter option is used in the Altair, a new derivative of the General Atomics Predator B.  This configuration allows for the thrust to be produced along the fuselage’s axis of symmetry, reducing the thrust-induced pitching moment.  Additionally, the lack of an external engine pod decreases parasite drag.  Due to these benefits, the embedded engine position is chosen and a standard rectangular to circular ducted configuration is incorporated into the design.

### 4.4.5 System Maintenance

With respect to system maintenance, the most obvious and bothersome aspect of the choice in propulsion arrangement is the embedded engine position.  This configuration presents the necessity of removing the power plant for all but the most basic system diagnostics and repairs.  However, the simplified systems and lightweight of the modified FJ44-1A eases the process of engine removal.  With a dry weight of less than 300 lb, the engine can be removed using standard mechanics pulley system.  In this way, long-term maintenance expenses are reduced, and an increased system lifetime is achieved.

## 4.6 Aerodynamics

The extreme altitude, range, and endurance required by the RFP are the driving factors for the aerodynamic design.  These are significant constraints, but the aerodynamic designer is free of other, more traditional configuration constraints.  The fuselage does not have to enclose a cockpit or a passenger cabin.  The RFP aircraft, being overpowered at sea level in order to climb to and cruise at 60,000 ft, will exceed traditional field performance requirements without the need of high lift devices.  Compressible effects, usually a strong factor in airfoil selection and planform geometry design, can be neglected in the RFP flight conditions of Mach 0.44 at cruise (no sweep required).

The most significant internal constraint is fuel storage.  To meet the range and endurance requirements, the aircraft is required to carry at least 1800 lb of fuel.  Most aircraft could easily carry this much fuel, but the altitude requirement places another major constraint on the design: the aircraft must be small and light.  Additionally, the trim drag must be kept at a minimum throughout the long missions.  This last constraint, as discussed during the selection process, requires that the fuel must be placed near the center of gravity.  The best way to place a large amount of fuel in the shortest possible longitudinal distribution is to use the wings as fuel tanks; thus the fuel constraint translates into a constraint on the airfoil thickness-to-chord ratio.

Another constraint on the wing thickness is structural weight.  This constraint, like the fuel capacity constraint, requires a thick airfoil—the thicker the wing spars, the lighter the structure.  The analysis, however, shows that the fuel capacity is the dominant driver of wing thickness, especially considering the lightweight carbon fiber box beam construction that is discussed in the structures section.

The goals of the aerodynamic design are to reduce the cruise drag to a minimum, achieve the appropriate lift-to-drag ratio to meet the range and endurance requirements, and promote an efficient, lightweight airframe.  The drag and lift-to-drag ratio goals can be achieved with an aircraft that minimizes three-dimensional flow, promotes a nearly elliptical spanwise lift distribution, and minimizes cross sectional and wetted surface area.

The aerodynamic analysis is presented in this section in the following subsections: Configuration Design, in which the choices of aircraft geometry are presented and justified; Airfoil, in which the airfoil choices and dimensioning are discussed; Computational Aerodynamic Analysis, in which the results of computer simulation iterations are discussed; and Final Aerodynamic Configuration, in which the final choices for aerodynamics are compiled and presented.

### 4.6.1 Configuration Design

The configuration design begins with incorporating the changes discussed at the end of the concept selection process into the design and justifying the changes with analysis.  A shorter, more compact aircraft is qualitatively desirable.  It is assumed that such an aircraft would create less drag and would be lighter and simpler.  Also, if the fuel were contained in the wings, the change in center of gravity position during flight would be small, eliminating the need for three pitch control surfaces.

To validate shortening the aircraft, a drag analysis of the old and new configurations is performed.  The Friction.f program, which calculates the viscous drag, requires the basic dimensions of the aircraft and the flight conditions.51  For simplicity, the aircraft’s fuselage and booms are modeled as cylinders and the wings are modeled as plates with finite thickness.  The flight conditions are taken from the cruise requirements of the RFP (60,000 ft, 250 ktas).  The Reynolds number for this aircraft at cruise is 840,000, which is above the limit for flat plate transition from laminar to turbulent flow (500,000).  This limit, however, can be exceeded by carefully choosing aerodynamic surface shapes that sustain favorable pressure gradients as long as possible.  With this in mind, laminar flow is assumed in the Friction.f calculations.

The analysis shows that the changes in configuration afforded an 11% reduction in wetted surface area and a reduction in drag coefficient of 8%.  The drag coefficient discussed here is the combination of friction drag and form drag, but does not include the induced drag, which is calculated in a later section.  These results justify the shortening of the aircraft and are presented in Table 28.

Table 28: The Results from Friction Analysis for the Shortened Aircraft

| Element | Value | Unit |
| --- | --- | --- |
| Total Swet | 550 | ft2 |
| Friction Drag | 0.01442 | - |
| Form Drag | 0.00237 | - |
| CD0 | 0.01679 | - |

The wing geometry design is driven by the need for very high efficiency at cruise.  The wing must also be structurally feasible and carry a large amount of fuel.  Since compressible effects are negligible at the cruise velocity, the wing is unswept.  A goal of the wing design is to achieve a high Oswald efficiency factor, approaching that of gliders.  The efficiency factor goal is 0.9, and is nearly achieved with an aspect ratio of 24.  This aspect ratio is close to the sizing goal of 23.25 and is structural feasible.  The Oswald’s efficiency factor of this configuration is calculated to be 0.88.

The A-tail design, originally conceived to reduce wetted surface area and structural weight, offers no gains in these areas.  Its justification is presented in the stability and control section.

The booms are designed to carry the following systems: landing gear, flight control, the navigation, and radar.  This arrangement frees space in the fuselage for the payload, engine, and fuel control system.  The savings are translated into a shorter, lighter aircraft.

### 4.6.2 Airfoils

The airfoil choices for the main wing and the empennage are presented and justified in this section.  Also, an analysis of the wings fuel capacity is performed to determine the thickness-to-chord ratio of the main wing.

Figure 31: The Main Wing Airfoil - NASA/Langley/Whitcomb LS(1)-0417 (GA(W))57

The main wing airfoil choice is the NASA/Langley/Whitcomb LS(1)-0417 (GA(W)) airfoil (Figure 31).  This class of airfoils shows excellent low speed characteristics and has good stall performance.  The maximum thickness, and therefore the position of the minimum pressures, is relatively far aft at 40% of the chord, and the change in thickness is small through the central part of the airfoil.  This arrangement delays the onset of an adverse pressure gradient and produces a gradual change in pressure over most of the airfoil.  The lift distribution shows an even spread along the length of the chord, with no sharp peaks near the leading edge.  These aerodynamic properties promote laminar flow and thus low drag.  The thickness of the central section of the airfoil is also desirable for fuel capacity and structural design.  This family of airfoils is used on Predator B, a successful high altitude UAV design.

The airfoil choice for the tail surfaces is a NACA 64-012 symmetric, laminar flow airfoil.  The thickness-to-chord ratio is chosen to be 0.12, which is a good compromise between low drag and structural design.  The airfoil section for the empennage is shown in Figure 32.

Figure 32: The Tail Surface Airfoil - NACA 64-01257

The choice of thickness-to-chord ratio for the main wing is strongly influenced by the fuel requirement.  The method for finding the appropriate ratio is present here.  A rectangle representing the product of the chord and the thickness is constructed.  The LS(1)-0417 family of airfoils takes up approximately 69% of the chord-thickness box.  A further deduction of 25% is made to account for the wing structure and flight control systems.  Using this area relationship and varying the thickness-to-chord ratio from 0.12 to 0.21, the graph in Figure 33 is constructed.

Figure 33: Main Wing Thickness-to-Chord Ratio and Wing Fuel Capacity

The target weight for fuel is 1800 lb, 1600 lb of which should be carried in the wings.  This target value, shown in the graph as a vertical line, leads to a thickness-to-chord ratio of 17.2%.  The ratio is set at 17%, leaving additional required fuel to be stored in the fuselage tank.

With the airfoils chosen, and the thickness-to-chord ratio set, a more detailed analysis of the flow over the airfoil is made.  First the inviscid solution of the flow over the LS(1)-0417 airfoil is found using a vortex lattice method code.20  The resultant velocity profile is then plugged into a code that calculates incompressible, laminar boundary layers with Waltz’s integral method.  This method, not accurate enough for detailed airfoil analysis, will provide enough information to test the assumption of laminar flow made in earlier analysis.  The calculation will show if the flow experiences transition, and approximately where that transition occurs.  The input information is presented in Table 29.

Table 29: Input Data for Boundary Layer Analysis

Fluid Properties Viscosity (m^2/s) = 1.222e-4

Reference Properties Freestream velocity (m/s) = 128.6 Reference length L (m) = 0.805

Surface Characteristics 2D body, rounded leading edge = 1 Pressure profile determined by velocity profile

Calculation Parameters Maximum x/L = 1 Number of x steps = 201

Figure 34 shows the results from the boundary layer calculation.  The upper plot shows the velocity profile (which is directly related to the pressure profile) and the bottom plot shows the boundary layer growth and location of the beginning of the transition.  The results indicate that the flow experiences transition at nearly 60% of the chord aft of the leading edge.  This transition is far enough aft to support the assumptions of laminar flow in the Fiction.f calculations, but could be improved upon.  Designing custom airfoils for specific aircraft has become an increasingly affordable option (X-Foil is a free airfoil design software package).  These airfoils typically exceed the performance of “off the shelf” airfoils, like the LS(1)-0417 (GA(W)).

Figure 34: Results from Boundary Layer Analysis

### 4.6.3 Computational Aerodynamic Analysis

The main tool used to analyze the aerodynamics of the design is Tornado, a MATLAB vortex lattice method code.54  The configuration is run through multiple iterations, systematically altering the wing area, aspect ratio, span, main wing incidence angle and location, tail boom length, tail surface area, and angle of attack.  These iterations and other analysis performed in the stability and control section lead to the final configuration, which is presented at the end of this section.

The Tornado program, like other vortex lattice programs, assumes irrotational and inviscid flow, but it differs form other codes in its treatment of the trailing vortices.  Instead of idealizing the trailing vortex system as a three-piece horseshoe, Tornado divides the vortex system into a seven-piece “sling,” allowing much more flexibility downstream of the wing.  This flexible wake more accurately models the complex interaction among multi-planar wings and allows Tornado to handle a wide variety of wing geometries.  Any number of wings, vertical surfaces, or stabilizers can be used, and each can be swept, tapered, cambered, twisted, or cranked.  Each can be programmed with or without dihedral, flaps, ailerons, elevators, rudders, winglets, fences, engine mounts, or any other variation that can be modeled as a planar surface.

The model is built up in Tornado by approximating the fuselage and the tail booms as NACA 0012 airfoils oriented in the z-plane.  The main wing is modeled with a NACA 4412 airfoil, since Tornado only accept 4-digit NACA airfoils.  Although this airfoil is not the appropriate choice for this type of aircraft, the data generated with it will offer a good baseline for performance, i.e. with the appropriate airfoil, the aircraft should exceed the performance predicted here.  The tail surfaces are constructed using NACA 0012 airfoils.  The configuration and pressure distribution are shown in Figure 35.

Figure 35: Model Layout and Pressure Distribution in Tornado

A grid dependence study reveals that the results are more dependent on chordwise panel spacing than spanwise spacing.  A grid with 6 chordwise panels and 16 spanwise panels is chosen as appropriate.  The calculations with this grid take as long a 3 hours to perform on a 1 GHz processor.  Given the large number of iterations required to optimize the geometry, methods to lessen the calculation time are desired.  A closer look at the contribution of the fuselage and tail booms reveals that they produce only 25 lb of lift and almost no induced drag.  Removing them from the model significantly reduces the computational time.  Therefore, the remaining calculations are made with the main wing and tail only.

Figure 36: Numerical Data Generated by Tornado Iterations (all forces in Newtons)

The numerical results from the Tornado iterations are presented in Figure 36.  The state fields indicate the flight conditions, which are 39.12 m/s equivalent sea level velocity, or 250 knots true air speed at 60,000 ft.  The angle of attack is 3.2 degrees (and the main wing angle of incidence is 1.5 degrees).  This flight conditions produces the design lift for steady flight, i.e. 3,025 lb.  The CL is low at 0.96 (the target is 1.1).  This low CL promotes low drag and leaves a large margin between the cruise CL and the stall CL of 1.8.  The coefficient of drag, as discussed above, only accounts for the induced drag, and is not appropriate for analysis on its own.  Adding the induced drag coefficient and the drag found by Friction.f, the drag coefficient becomes 0.029.  These coefficients combine to form a lift-to-drag ratio of 33.1.

The wing loading, which reflects the high Oswald efficiency factor (0.88), is presented in Figure 37.

Figure 37: Span Loading Generated by Tornado

The final properties of the aero dynamic configuration are presented in Table 30.

Table 30: Final Aerodynamic Properties

| Element | Value | Unit |
| --- | --- | --- |
| S | 160 | ft2 |
| b | 62 | ft |
| AR | 24.0 | - |
| Oswald e | 0.88 | - |
| CL @ Cruise | 0.96 | - |
| CD @ Cruise | 0.029 | - |
| Re @ Cruise | 840,000 | - |
| L/D | 33.1 | - |
| MAC | 2.64 | ft |
| Wing inc. | 1.5 | deg |
| ( | 3.2 | deg |

## 4.7 Stability and Control

The goal of the stability and control analysis is to justify the configuration geometry, characterize the longitudinal stability of the aircraft, and size the control surfaces.  These goals are accomplished using a combination of empirical and theoretical design tools.45

### 4.7.1 Justification of Configuration Geometry

The aircraft’s layout—a low wing monoplane with a pitch-yaw control tail—is time tested and well understood.  The only unconventional feature that requires justification is the A-tail configuration.  Traditionally, the pitch-yaw control would be actuated with separate appendages and control surfaces: pitch controlled by a horizontal tails and elevators; yaw controlled by a vertical tails and rudders.  This traditional arrangement, however, can be heavy and can result in a large amount of wetted surface area.  The A-tail, as shown in Figure 38, was conceived to save in these two areas, structural weight and wetted surface area.  But research revealed that in order maintain the same control effectiveness the area of the A-tail surfaces must be sized up to such an extent that the weight and surface area savings are negated.45  A closer look at the A-tail from a stability and control perspective, however, produces an unexpected justification for the A-tail: a proverse roll yaw coupling.

Figure 38: Detail of the A-tail and Communications Pod

A traditional tail arrangement for tail booms involves two vertical surfaces and a connecting horizontal surface.  More recently, as seen on the successful high altitude UAV Predator B, a V-tail has gained favor among configuration designers.  Both these arrangements, however, produce an adverse roll-yaw coupling, i.e. when a nose right yaw is desired, the aircraft rolls left.  This adverse roll must be countered with large aileron deflections and the associated increases in drag.

Figure 39 illustrates the roll-yaw coupling phenomenon and shows how the A-tail avoids takes advantage of it.  Looking forward on the aircraft, and assuming the center of gravity is located at the center of the fuselage, it is easy to see that the forces required to produce a nose right yaw will produce a right roll in both the V-tail and the traditional tail.  The same maneuver actuated by the A-tail produces a favorable roll-yaw coupling, and reduced drag during the maneuver.  In addition to this control advantage (which alone could justify the configuration), the A-tail works well with the engine and boom layout and affords convenient placement of the satellite communication dome.

Figure 39: Illustration of Roll-Yaw Coupling

### 4.7.2 Static Margin

The static margin of typical commercial transport aircraft is between 5% and 10% stable.  This level of longitudinal stability produces aircraft that pilots can handle easily and that can fly efficiently in many different loading conditions.  But the gains in handling qualities and center of gravity range come at the price of trim drag at cruise and reduced maneuverability.  Typical fighter aircraft, primarily concerned with maneuverability, fly with static margins between 0% and 15% unstable.  The gains in maneuverability come at the cost of a more complex flight controls system and larger control surfaces.

The static margin for Menelaus will fall between that of a typical transports and fighters.  Since the aircraft will be unpiloted, the handing characteristic can be more challenging than a commercial pilot would care to experience on a long flight.  But the maneuverability of a fighter is not required, nor is the complexity of a fighter’s flight control system.  So the goal for Menelaus is to achieve the minimum trim drag at cruise without going unstable as the fuel is consumed.  This goal requires the aircraft to fly as close to neutral as possible during cruise, but with a sufficient margin for in flight center of gravity shifts.  A goal is set to keep the static margin between 0% and 5% stable.

An iterative process is used to achieve the design static stability.  The process takes into account the changes in longitudinal center of gravity position during a typical mission.  The location of the main wing, the length of the booms, and the size of the A-tail surfaces are systematically altered, and the stability derivatives are calculated with Tornado.  A typical, beginning of mission Tornado output is shown in Figure 40.

Figure 40: Tornado-Generated Stability Derivatives

The static margin is calculated using the moment equation developed in any stability and control text.22

Kn = (hn – h) = -(Cm-alfa/CL-alfa)

Here, Kn is the static margin, hn is the distance from the leading edge of the mean aerodynamic chord to the neutral point (normalized to the mean aerodynamic chord), and h is the normalized location of the center of gravity.  Using Tornado’s notation, Cm-alfa is the change in moment with respect to the change in angle of attack, and CL-alfa is the change in lift coefficient with respect to the change in angle of attack.

These iterations result in a static margin that is 2.2% stable at the beginning of the mission and 0.5% stable at the end of the mission (with 3% of the fuel remaining).

### 4.7.3 Control Surface Sizing

Typical aircraft design sizing algorithms for control surfaces generally result in control surfaces that were too large for Menelaus.  Therefore, existing high altitude, long endurance/range aircraft are used as a guide for surface sizing, and Tornado is used to validate the choices.

For aileron sizing, a rule of thumb approach leads to surfaces that are 20% to 25% of the wings chord, and extend from 50% to 90% of the wing’s semispan.45  Ailerons of this size, place so far outboard, would most likely result in control reversal for such a high aspect ratio wing, and are unnecessary for the types of maneuvers Menelaus is expected to perform.

Figure 41: Perseus B Aileron Size and Location39

Perseus B, designed be Aurora Flight Sciences, is a high altitude UAV that closely matches the size of Menelaus.  The photograph in Figure 41 shows the size and location one of the ailerons.  The surface is about 15% of the chord in the chordwise direction and 20% of the semispan in the spanwise direction.  It is located between 40% and 60% of the semispan outboard.  Tornado analysis, however, shows that these surfaces are too small for Menelaus.  Sizing them up to 20% of the chord and 28% of the semispan and locating them between 39% and 67% of the semispan outboard lead to reasonable results from Tornado.  The resultant ailerons are 4.2 ft2 each and are shown in Figure 42.

Figure 42: Menelaus Aileron Size and Location (all dimensions in ft)

The V-tail ruddervators on Predator B, a General Atomics high altitude UAV, are used as a model for the A-tail surface sizing.  Although the V-tail and A-tail look different and produce different roll-yaw coupling, they are required to generate essentially the same forces for controlling the aircraft.  The size of the control surfaces should be the same.  Predator’s control surfaces are shown in Figure 43.  They are about 20% of the chord in the chordwise direction and extend the entire length of the tail surface in the spanwise direction.  To make up for the extra control force Predator generates with the ventral vertical surface, the ruddervators for Menelaus are sized up to 25% the chord in the chordwise direction.  Tornado analysis shows this sizing is reasonable, and the resultant ruddervators, which are 2.4 ft2 each, are shown in Figure 44.

Figure 43: Predator B Ruddervator Size and Location39

Figure 44: Menelaus Ruddervator Size and Location (all dimensions in ft)

## 4.8 Performance

Many aircraft exist that some or most of the RFP requirements.  The central justification of this design project is to improve upon previous designs and to generate a viable platform that meets all of the RFP requirements.  The quantitative measures of mission success are the Menelaus performance characteristics.  In this section, the aircraft design’s performance is calculated and compared to the RFP requirements.

### 4.8.1 Mission Profile Analysis

The Virginia Tech Mission Program is used to calculate the design aircraft’s performance.  The measures of effectiveness are taken from the RFP and are listed as follows: cruise altitude (60,000 ft), range (7,000 NM), endurance (36 hours), and time to climb (90 minutes).

The following two missions were modeled in the mission analysis program:

1 – Twenty Minute Loiter Time at Full Thrust (simulating taxi, etc…)

2 – Climb to 60,000 ft. Using Best Rate of Climb

3 – Cruise at 60,000 ft. at Mach 0.44 for over 8,000 NM

4 – Descend to Sea Level

1 – Twenty Minute Loiter Time at Full Thrust (simulating taxi, etc…)

2 – Climb to 60,000 ft. Using Best Rate of Climb

3 – Cruise at 60,000 ft. at Mach 0.38 for over 7,000 NM

4 – Descend to Sea Level

Analysis of the two outputs serves to validate the ability of Menelaus to meet all of the RFP requirements.  In both cases, more than a 300 lb of fuel remains at the end of the mission; therefore the missions are plausible.  In the first mission a sea level climb rate of 3,400 ft/min is registered along with a cruise Mach number of 0.44.  Since the range exceeds the requirement and the endurance is short of the requirement, Mach number in the second run is lowered to 0.38.  The result an increase in endurance from 34.5 hours to 37 hours and a decrease in range from 8,300 NM to 7,400 NM.  From these profiles it is shown that the cruise Mach number and climb rate can be increased well beyond the RFP requirements.

The Mach 0.44 profile is demonstrated graphically below in Figure 45.

Figure 45: Optimal Mission Profile

### 4.8.2 Aircraft Comparison

Justification for the Menelaus program is seen in a comparison between the aforementioned aircraft and those comparable systems, as seen in Table 31.

Table 31: Menelaus Comparison

4.9 Materials and Structure

### 4.9.1 Materials

Since the Menelaus is a proof of concept aircraft, the main driving factors for the structural design are as follows:

1) Weight

2) Strength

3) Cost

Table 32 shows the comparison of approximate material cost when the Menelaus is constructed with different materials for each major component.  The heaviest configuration is the one in which all major components are constructed with Aluminum.  The lightest configuration is the one in which the wings, A-tail, fuselage, and booms are constructed with carbon fiber and landing gear, engine mount, and payload interface is constructed with Aluminum.  Carbon fiber is approximate 50% lighter and 500% more expensive than Aluminum.  Carbon fiber also comes with higher tensile and yield strength per unit weight than Aluminum.  Although the mostly carbon fiber aircraft is easily the most expensive, mission analysis has shown that it is the only configuration that can meet the RFP requirements.

Table 32: Approximate Material Cost58

| Components |  | Materials | Weight |  | Components |  | Materials | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | lb |  |  |  |  | lb |
| Wings |  | Al | 700.00 |  | Wings |  | CF | 350.00 |
| H. Tail |  | Al | 42.00 |  | H. Tail |  | CF | 21.00 |
| V. Tail |  | Al | 14.00 |  | V. Tail |  | CF | 7.00 |
| Fuselage |  | Al | 255.60 |  | Fuselage |  | Al | 255.60 |
| Booms |  | Al | 108.77 |  | Booms |  | Al | 108.77 |
| Landing Gear |  | Al | 148.20 |  | Landing Gear |  | Al | 148.20 |
| Installed Engine |  | Al | 260.00 |  | Installed Engine |  | Al | 260.00 |
| Payload |  | Al | 250.00 |  | Payload |  | Al | 250.00 |
|  |  | Total | 1778.57 |  |  |  | Total | 1400.57 |
|  |  | Approximate Material |  |  |  | Approximate Material |
|  |  | Cost | $1,908 |  |  |  | Cost | $4,105 |
| Components |  | Materials | Weight |  | Components |  | Materials | Weight |
|  |  |  | lb |  |  |  |  | lb |
| Wings |  | Al | 700.00 |  | Wings |  | CF | 350.00 |
| H. Tail |  | CF | 21.00 |  | H. Tail |  | CF | 21.00 |
| V. Tail |  | CF | 7.00 |  | V. Tail |  | CF | 7.00 |
| Fuselage |  | Al | 255.60 |  | Fuselage |  | CF | 127.80 |
| Booms |  | Al | 108.77 |  | Booms |  | CF | 54.38 |
| Landing Gear |  | Al | 148.20 |  | Landing Gear |  | Al | 148.20 |
| Installed Engine |  | Al | 260.00 |  | Installed Engine |  | Al | 260.00 |
| Payload |  | Al | 250.00 |  | Payload |  | Al | 250.00 |
|  |  | Total | 1750.57 |  |  |  | Total | 1218.38 |
|  |  | Approximate Material |  |  |  | Approximate Material |
|  |  | Cost | $2,807 |  |  |  | Cost | $19,906 |
| Components |  | Materials | Weight |  | Components |  | Materials | Weight |
|  |  |  | lb |  |  |  |  | lb |
| Wings |  | CF | 350.00 |  | Wings |  | Al | 700.00 |
| H. Tail |  | Al | 42.00 |  | H. Tail |  | Al | 42.00 |
| V. Tail |  | Al | 14.00 |  | V. Tail |  | Al | 14.00 |
| Fuselage |  | Al | 255.60 |  | Fuselage |  | Al | 255.60 |
| Booms |  | Al | 108.77 |  | Booms |  | CF | 54.38 |
| Landing Gear |  | Al | 148.20 |  | Landing Gear |  | Al | 148.20 |
| Installed Engine |  | Al | 260.00 |  | Installed Engine |  | Al | 260.00 |
| Payload |  | Al | 250.00 |  | Payload |  | Al | 250.00 |
|  |  | Total | 1428.57 |  |  |  | Total | 1724.18 |
|  |  | Approximate Material |  |  |  | Approximate Material |
|  |  | Cost | $4,001 |  |  |  | Cost | $2,905 |
|  | Name |  | Density | Tensile strenght, Yield | Cost Unit | Ratio Force/Weight |  |
|  | Aluminum Alu 6061-T4 | 2.7 | 145 | 0.8 | 53.7 |  |
|  | Basic Carbon Fiber Composite | 1.57 | 200 | 5 | 127.4 |  |

### 4.9.2 V-n Diagram

The V-n diagram in Figure 46 shows the limitations for loading based on velocity.  The maneuver envelope is less important to the design than is the gust envelop, since no high g maneuvers are anticipated.  The structure was designed for a positive ultimate load of 4.04 and a negative ultimate load of -2.04.

Figure 46: V-n Diagram

### 4.9.3 Wing Elements

The wing of the Menelaus is constructed with a bi-directional carbon fiber-Nomex honeycomb core sandwich skin.  This outer layer is stiffened with integral stringers to resist buckling and assist in the load carrying capacity.  The stiffeners are arranged to create two box beams.  These beams carry the wing load into the fuselage, where they are attached to two bulkheads.  Wing frames are distributed every 3 ft along the wing.  This will leave approximately 75% of the wing’s volume for ample fuel tank in each wing.  The wing structures are shown in Figure 47.

Figure 47: Wing Structure

### 4.9.4 Fuselage

The fuselage is also constructed with bi-directional carbon fiber-Nomex sandwich to minimize the weight of the aircraft.  The composite skin is stiffened with integral stringers to resist buckling.  The main structural skeleton of the fuselage includes two bulkheads and three ring frames.  The bulkheads are located at the main wing.  One ring frame is located where the payload is attached, and two ring frames are located where the engine is installed.  Figure 48 shows the fuselage structure.  Eight tophat stiffeners and a 3-inch ring frame stiffen the sandwich skin.  Figure 49 show the connection of the nose cone and the ring frame.  The nose cone is modular and removable as one piece.

Figure 48: Fuselage Structure

Figure 49: Nose Cone Connection

### 4.9.5 Tail Booms

The booms are similarly constructed to the fuselage except the location of the ring frames, which are located at the highly loaded areas along the booms.  The ring frames are placed at the wing intersection, aft of the main landing gear bay, and at the A-tail.

### 4.9.6 Weights Breakdown

The weights summary is listed in Table 33.  It shows the weight of each component calculated using one of the three methods: Raymer’s Method in chapter 15, estimating from existing systems, or determined by the RFP.45

Table 33: Weight Summary

| Components |  | Weight | Xcg | Moment |
| --- | --- | --- | --- | --- |
|  |  |  | (lb) | (in) | (in-lb) |
| Structures |  |  |  |  |
| Fuselage |  |  | 283 | 120.00 | 25454.83 |
| Booms |  |  | 80 | 236.40 | 14142.57 |
| H. Tail |  |  | 9 | 6.40 | 2227.30 |
| V. Tail |  |  | 20 | 348.00 | 5304.94 |
| Wings |  |  | 2032 | 154.20 | 235023.50 |
| Main Gear |  |  | 98 | 154.20 | 15091.58 |
| Nose Gear |  |  | 26 | 112.80 | 2920.13 |
| Composite Struc. Saving |  | -606 |  |  |
| Propulsion |  |  |  |  |
| Engine |  |  | 449 | 220.80 | 99195.89 |
| Systems |  |  |  |  |
| Fuel |  |  | 60 | 154.20 | 9243.96 |
| Flight Control |  | 28 | 236.40 | 6567.78 |
| Hydraulics |  |  | 3 | 154.20 | 462.60 |
| Avionics |  |  | 81 | 236.40 | 19253.40 |
| Electrical |  |  | 157 | 120.00 | 18846.61 |
| Payload |  |  | 250 | 63.60 | 15900.00 |
| Com. Sys. |  |  | 30 | 348.00 | 10440.00 |
| TOGW |  | 3000 | 13.34 | 40006.26 |

### 4.9.7 Center Of Gravity Travel

The center of gravity changes during the flying mission.  The cg location change of the Menelaus is shown in Figure 50.  It can be seen that the cg location does not change very much during the RFP mission since most of the weight of the aircraft comes from the fuel, which is located in the wings near the cg location.

Figure 50: Center of Gravity Travel

## 4.10 Systems

### 4.10.1 General Layout

The general layout of the aircraft is shown in Figure 51.  The payload is housed in the nose of the fuselage and is completely removable.  Just aft of the payload is the avionics suite and systems that support the payload instruments.  The fuel is stored in a small tank in the fuselage and two large tanks in the wings.  The fuel system is placed aft of the main wing, just forward of the engine, which is mounted in the aft end of the fuselage.  The radar and collision avoidance system is situated in the noses of the tail booms.  The main landing gear fold aft into storage bays in the tail booms, just aft of the main wing.  The remaining volume in the booms is filled with the flight control and navigation systems.  The satellite communications system is located at the apex of the A-tail.

Figure 51: General Layout of Systems

### 4.10.2 Payload System

The payload bay is located in the nose cone of the Menelaus.  The payload interface complies with the power and information exchange requirements needed by the MicroMAPS-Proteus interface.  An onboard LAN system will be used as the method of data transfer.  Electric power will be derived from the aircraft engine and routed through a transformer and a series of devices designed to “clean” the current.

### 4.10.3 Fuel System

The aircraft requires 1800 lb of fuel, including the reserves.  One thousand six hundred pounds of fuel is held internally in the integral wing tanks, and two hundred pounds is held in the fuselage tank located at the wing root.  Fuel pumps, filters, and valves are located aft of the main wing, just forward of the engine.  The fuel is first drained from the wing tanks equally; then drained from the fuselage tank.

### 4.10.4 Landing Gear

The main landing gear is located 0.67 ft aft of the center of gravity making 15 degrees from the center of gravity of the aircraft.  The nose gear is located 6.7 ft forward of the landing gear.  The main landing gear is 2.5 ft long and supports a load of 2,700 lb.  The nose gear is 3.54 ft long, making 45 degrees to the aircraft, and supports a load of 300 lb.  This arrangement is shown in Figure 52.

Figure 52: Landing Gear Arrangement (dimensions in ft)

### 4.10.5 Communication

As Menelaus will operate well beyond visual range, one must choose between the use of several pre-arranged ground stations and a satellite communication interface.  The satellite system is preferable due to its constant coverage of a large area and readily available technology.  The satellite communication equipment is to be located at the apex of the A-tail.  This provides for an unobstructed line of sight for the communication signals and limits the effect of electromagnetic corruption of science data being taken in the nose and avionics equipment located throughout the craft.

### 4.10.6 Avionics

Menelaus, being unpiloted, requires constant control via the analysis of flight data and position information preformed by control equipment.  This equipment is to be stored in the tail booms.  Technologies previously adapted for use in UAVs, such as Predator B, can be used.

### 4.10.6 Flight Controls

Flight control is to be accomplished via a series of electronic torque generating actuators.  The system priority shall be lifetime and ease of maintenance as opposed to devises built for the exertion of large loads.  This is due to the flight envelope of Menelaus being limited to relatively slow speeds and the lack of dramatic maneuvering through the course of the given mission.  Additionally, this system will decrease weight below that of hydraulic systems.

## 4.11 Cost Analysis

Satisfying the proposal’s required parameters is not the only necessity to win the contract in today’s competitive world.  The lowest or most affordable price is required for the better chance to win the contract.  The cost of the Menelaus was calculated by using RDT&E method.45  The cost of the Menelaus includes engineering hour cost, tooling hour cost, manufacturing hour cost, development support cost, flight test aircraft cost, material cost, manufacturing material cost, and engineering production cost.  Table 34 shows the breakdown of RDT&E cost analysis.  In keeping with standard economics, as the number of units produced is increased, the cost per unit decreases.  This decrease in unit cost is most crucial in the initial product orders, as witnessed in Table 34 and Figure 53.  A per unit price decrease of 80% occurs upon the sale of five units, as opposed to one.

Table 34: Breakdown of RDT&E Cost Analysis

| Category | Cost |
| --- | --- |
| Engineering Hours | $361,097.13 |
| Material Cost | $19,906.64 |
| Tooling Hours | $175,116.74 |
| Manufacturing Hours | $167,867.15 |
| Development Support Cost | $8,390,142.00 |
| Flight Test Aircraft | $1,790,930.38 |
| Manufacturing Materials Cost | $1,433,445.72 |
| Engineering Production Cost | $822,976.86 |
| Total 1 Unit | $13,141,575.98 |
| Total 5 Units | $2,628,315.22 |

Figure 53: Percentage of RDT&E Cost

## 4.12 Final Proposal

Menelaus was designed to be completely responsive to the RFP.  The design choices to achieve the RFP goals have lead to a high-altitude, long-range, long-endurance UAV for atmospheric remote sensing.  The aircraft is a turbofan-powered,* low-wing, high aspect ratio monoplane with an axi-symmetric fuselage and tail booms.  The payload is situated in a modular fuselage nosecone, which is removable in one piece, and can be modified to rotate about it axis of symmetry for instrument pointing.  The A-tail offers desirable roll-yaw coupling and supports the satellite communications system at its apex.  A three-view drawing of the aircraft is presented in Figure 54 at the end of this section.

Table 35 shows a comparison between the major RFP requirements and Menelaus.  The altitude, cruise velocity, time to cruise, and payload requirements are all met.  The aircraft exceeds the range requirement, and is within 5% of the endurance requirements.  Both the range and endurance targets can be met simultaneously by slowing the cruise velocity slightly.

Table 35: Comparison with RFP

| Item | RFP | Menelaus | Comment |
| --- | --- | --- | --- |
| Altitude Range Endurance Vcruise Climb Time Modular Payload | > 60.000 > 7,000 > 36 hrs 250 ktas < 90 min < 250 lb | > 60.000 > 8,000 34.2 hrs 250 ktas < 84 min < 250 lb | OK Exceeds Close OK OK OK |

By meeting or exceeding the RFP requirements, Menelaus achieves all the advantages an aircraft platform has over a space-based platform.  These were listed in the RFP and include the following: lower cost (no launch cost), opportunities for maintenance (without astronauts), mission flexibility, and payload flexibility.  The performance of this aircraft (altitude, range, endurance) offers scientists new and unique data gathering opportunities impossible only a few years ago.  The low cost opens up these opportunities to scientists who cannot afford a space mission with a price tag of at least tens of millions of dollars.  As indicated in the RFP, a need exists for high quality, inexpensive alternative to space-based atmospheric remote sensing platforms, and Menelaus is the answer.

Figure 54: Menelaus Three-View

# Chapter 5: Aiolos

A spacecraft carrying the MicroMAPS instrument would likely be built and operated by NASA or by contractors working with the agency.  In this situation, the possibility exists that NASA would choose to design a spacecraft platform that would conduct several science missions from orbit around the Earth.  The spacecraft designed for this project, however, is to carry only one science instrument (MicroMAPS).  Such a design leads to the assumption that the mission would have a relatively small budget, making cost a significant driver in the design process.  As explained in the following sections, the attempt to reduce cost impacts major decisions such as not including a propulsion system, launching as a secondary payload, and minimizing the amount of redundancy in the spacecraft systems.  The spacecraft is named Aiolos after the Greek god of the winds, since the mission calls for the study of the atmospheric transport processes.

## 5.1 Orbit Design

The science requirements of the MicroMAPS instrument place several restrictions on the spacecraft orbit design.  Since there is only one instrument, formation flying or constellation missions are not feasible.  Due to the nature of the science data, the instrument can only operate from low Earth orbit (LEO).  In general, the science mission requires coverage of a high percentage of the Earth’s surface, an indicator that high inclination orbits should be used.

### 5.1.1 Specialized Orbits

Two specialized orbits, polar and sun-synchronous, are possibilities for high inclinations at LEO.  A polar orbit has an inclination of 90° and therefore can take science data over all of the Earth.  As discussed later, the primary areas of interest to the science mission do not include the polar regions.  For this reason, the polar orbit is not used so that a higher percentage of the mission’s lifetime is spent taking useful science data.

The other possible specialized orbit is a sun-synchronous orbit.  Due to the effects of the perturbations on this orbit, the orientation of the orbital plane with respect to the sun stays constant.  Since the spacecraft passes through the orbit’s ascending node at the same solar time during every orbit, the surface of the Earth can be viewed under consistent lighting conditions.  This feature would be useful for MicroMAPS, as the orbit could be chosen to minimize the interference from clouds in the atmosphere.  Yet, this situation is not optimal for MicroMAPS, as a need exists to understand how carbon monoxide distribution changes over the course of a day.  In addition, a sun-synchronous orbit requires a propulsion system, which significantly increases the mission cost.  Primarily for these two reasons, the sun-synchronous orbit is not chosen for the Aiolos design.

### 5.1.2 Propulsion

The inclusion of a spacecraft propulsion system is an important consideration for orbit design.  Propulsion makes orbit control possible, which is advantageous because the spacecraft could maintain a consistent altitude for the MicroMAPS instrument.  A changing altitude, however, is not a concern as the instrument can compensate for this change with little impact on the science data.13  A propulsion system also adds considerable cost to the mission.  This cost ranges from $1 million for a huge and heavy cold gas system to several million dollars for hydrazine, bipropellant, or electic propulsion systems.2  A propulsion system is not included in the Aiolos design since the science mission benefit does not justify the cost.

### 5.1.3 Altitude

Aiolos cannot prevent orbital decay without a propulsion system.  Orbital decay is caused by atmospheric drag, eventually causing the spacecraft to burn up in the Earth’s atmosphere.  The most important consideration for the beginning of life (BOL) altitude is the lifetime desired for the science mission.  Since the variation in carbon monoxide data from one year to another is of interest to scientists, the operational goal for Aiolos is three years.  For this mission, end of life (EOL) is considered to be at an altitude of 300 km.  Designing spacecraft systems to operate below this altitude is impractical and at 300 km, less than two months remain before the spacecraft burns up in the atmosphere.61  This mission uses a circular orbit in order to provide approximately consistent viewing conditions for the science instrument throughout a given orbit.

Orbit decay rate () is determined by Eq. (5.1) where r is the orbit radius, ( is atmospheric density, CB is ballistic coefficient and P is the orbit period.

(5.1) 61

The ballistic coefficient is determined by the physical characteristics of the spacecraft.  The orbit radius and period are determined by altitude, and the atmospheric density is determined by both altitude and the solar cycle.  One way to maximize the spacecraft lifetime at a given altitude is to launch when solar activity is at a minimum.  The next minimum in the solar cycle occurs in 200761, and as such, an ideal launch date for Aiolos would be June 2007.  Table 36 lists the values of atmospheric density at 50 km increments during minimum solar activity.

Table 36: Atmospheric Densities at Minimum Solar Activity 61

| Altitude (km) | Density (kg/m3) |
| --- | --- |
| 450 | 2.47 ( 10-13 |
| 400 | 7.32 ( 10-13 |
| 350 | 2.34 ( 10-12 |
| 300 | 8.19 ( 10-12 |

For the purposes of lifetime analysis, an orbital decay rate is calculated for each 50 km segment using the above equation and the average atmospheric density for each individual altitude segment.  The time spent in each range of altitudes is then calculated based on dividing 50 km (or 25 km, as in the case of the first segment) by each orbital decay rate.  These values are compiled in Table 37.

Table 37: Orbital Decay Calculations

| Altitude Segment (km) | Orbital Decay Rate (km/s) | Time Between Altitudes (days) |
| --- | --- | --- |
| 425 - 400 | -3.4 ( 10-7 | 840 |
| 400 - 350 | -1.1 ( 10-6 | 540 |
| 350 - 300 | -3.7 ( 10-6 | 160 |

Using this information, the summation of the times for each segment gives an estimate of the lifetime for the spacecraft.  This information indicates that if the BOL altitude is 425 km, the total time until EOL (300 km) is about four years.  This altitude, therefore, provides some margin to account for the inaccuracy of the atmospheric model in both altitude and time as the solar cycle progresses.  Using a BOL altitude of 425 km, the three year lifetime is met.

### 5.1.4 Inclination

Another major component of orbit design is the inclination of the orbit with respect to the equator.  This characteristic determines the range of latitudes over which the MicroMAPS instrument takes science data.  The two primary sources of carbon monoxide are densely populated, developing countries and biomass burning in various parts of the world.13  Figure 55 shows population density throughout the world, the densest areas colored in red.

Figure 55: World Population Density63

The primary transport processes on the Earth move east to west, meaning that coverage is necessary up to the most extreme latitudes where carbon monoxide production is a major concern.  As the figure above shows, the most extreme region with a high population density is Europe, at nearly 60° north latitude.  Launching the spacecraft into an orbit inclined 60° to the equator provides all the necessary coverage for carbon monoxide produced from both population density and biomass burning.  For the purposes of launch vehicle selection, the final desired orbit inclination is set at 64°.

### 5.1.5 Orbit Determination System

Another consideration for orbit design is how orbit determination will be completed.  Historically, most missions have used ground stations or the Tracking and Data Relay Satellites (TDRS) to track spacecraft.  Ground based tracking usually requires several orbits and achieves results of several kilometers for LEO.61  The TDRS system provides nearly complete coverage for LEO with an accuracy on the order of 50 meters.61  This type of system can be used as a backup for Aiolos, but this spacecraft takes advantage of the benefits of a Global Positioning System (GPS) for orbit determination.

Increasing numbers of spacecraft are using GPS for navigation requirements in LEO.  Such a system provides autonomous and real-time orbit determination by providing the position and velocity of the spacecraft in addition to a highly accurate measure of the current time.  The GPS orbit determination system is an improvement over the accuracy of ground based tracking and has low costs.

Surrey Satellite Technology Ltd (SSTL) is a manufacturer of small satellites and subsystems, including Space GPS Receivers (SGR).48  The SGR-10 model suits the goals of the Aiolos mission.  This receiver includes two antennas that provide position, velocity, and time measurements.  Important data about the SGR-10 is included in Figure 56, and a picture of SGR-20 is shown in Figure 56.  The only significant difference between SGR-10 and SGR-20 is that SGR-20 has four antennas instead of two.

Table 38: SGR-10 Data48

| Description | Value |
| --- | --- |
| Position Accuracy (2 sigma) | 15 m |
| Velocity Accuracy (2 sigma) | 1.5 m/s |
| Thermal Operating Range | -20 to +50 °C |
| Size | 160 ( 160 ( 50 mm |
| Mass | 1 kg |
| Power Consumption | 5.5 to 7 W |
| Power Supply | 28 or 5 V |

Figure 56: SGR-20 Receiver and Antennas48

## 5.2 Attitude Determination and Control System (ADCS)

The science goals of the MicroMAPS instrument require the spacecraft to be nadir-pointing during data collection.  The specific attitude determination and control requirements are well defined by the instrument specifications.  Aiolos is required to have attitude knowledge to within (0.5° and to be able to control the attitude to within (2.5° of nadir.46  Sensors and actuators that can meet these requirements must be selected for use on the spacecraft.

Two forms of attitude control systems can be used for a nadir-pointing mission: gravity-gradient and three axis stabilization.61  Gravity gradient stabilization can only be the primary method of control for requirements greater than 5°.61  Aiolos, therefore, uses a three axis primary control scheme but is also configured to take advantage of gravity-gradient stabilization.

### 5.2.1 Control Modes

During a mission, ADCS may have several different modes of operation, depending on the goals of the particular mission segment.  These modes can include orbit insertion, acquisition, normal, slew, safe, and special modes.61  Aiolos uses an acquisition mode to stabilize the vehicle following launch and a safe mode for emergencies on the spacecraft.  The primary mode, however, is the normal mode during which the spacecraft completes the science mission.  The ADCS is designed to operate in this mode throughout the vast majority of the spacecraft lifetime.

### 5.2.2 Attitude Determination Components

A wide variety of attitude sensors are typically used on space missions, including gyroscopes, sun sensors, horizon sensors, star trackers, and magnetometers.  Sun sensors, horizon sensors, and magnetometers are appropriate for this mission due to their relatively low cost, low weight, and high reliability. 61  GPS receivers are also considered, but attitude determination using GPS is a relatively new concept.  Due to the small size of Aiolos, GPS receivers are unlikely to provide the attitude knowledge needed for this mission.27

A horizon sensor provides pitch and roll knowledge to the spacecraft.  Ithaco Space Systems builds a Conical Earth Sensor (CES) which meets the requirements of Aiolos.  The CES is flight proven, as over 40 of the sensors have been flown on NASA and DoD missions, demonstrating an accuracy of 0.1°.4  This sensor is vital to the completion of the Aiolos mission, as it is the primary source for pitch and roll data.  Accordingly, two of the sensors are flown on the spacecraft to provide redundancy should one fail.  The CES is shown in  instrument information is provided in Table 39.

and instrument information is provided in Table 39.

Figure 57: Ithaco Conical Earth Sensor4

Table 39: Ithaco Conical Earth Sensor Specifications4

| Description | Value |
| --- | --- |
| Accuracy | 0.1° |
| Size, Sensor Head | 9.9d ( 11.8 cm |
| Size, Electronics | 16.8 ( 17.0 ( 8.3 cm |
| Mass, Sensor Head | 1.1 kg |
| Mass, Electronics | 1.9 kg |
| Power Consumption | 8 W |
| Input Voltage | 22-36 or 31-52 V |

For complete attitude determination, knowledge of the third axis, yaw, must be provided.  Aiolos uses sun sensors and a magnetometer to complete the attitude determination instrument suite.  While yaw data are not vital to the science mission, such information does help to maintain the desired spacecraft orientation throughout the orbit.  Aiolos uses five sun sensors produced by SSTL (Figure 58) as the primary source of yaw data.  The two axis sensors provide data for azimuth and elevation to the sun at an accuracy of 0.5°.48  The five sensors are distributed over the spacecraft to provide data on the sun’s position while Aiolos is in daylight.  This arrangement is designed to maximize the time that the sun vector is known so that the solar arrays can be most efficient.  Data on the sun sensors are provided in Table 40.

Figure 58: Surrey Two Axis Sun Sensor48

Table 40: Surrey Sun Sensor Specifications48

| Description | Value |
| --- | --- |
| Accuracy (Three Sigma) | 0.5° |
| Sensor Field of View | ( 50° |
| Operating Temperature | -50 to 80°C |
| Size | 95 ( 107 ( 35 mm |
| Mass | 0.3 kg |
| Power Consumption (sunlit) | 100 mW |
| Power Supply | ( 12 V |

While Aiolos is in eclipse, a magnetometer can be used to determine the yaw orientation of the spacecraft.  Magnetometers do not generally provide the accuracy of a sun sensor but are particularly useful in conjunction with the magnetic torquers used for attitude control.61  Ithaco produces a three axis magnetometer, IM-103, that meets the needs of Aiolos.  Ithaco has demonstrated high reliability through the successful deployment of over 175 magnetometers.4  The IM-103 is shown in Figure 59 and information on the magnetometer is in Table 41.

Figure 59: Ithaco IM-1034

Table 41: Ithaco IM-103 Specifications4

| Description | Value |
| --- | --- |
| Operating Temperature | -40 to 80°C |
| Size | 5.5 ( 4.2 ( 3.6 cm |
| Mass | 227 g |
| Power Consumption | 1 mW |
| Supply Voltage | ( 15 V |

### 5.2.3 Disturbance Torques

Before selecting attitude control components, the attitude disturbance environment must be characterized.  Four disturbance torques are considered: gravity-gradient (Tg), solar radiation (Tsp), magnetic field (Tm), and aerodynamic (Ta).  The following equations are used for the calculations.61  Definition of the variables is included in Table 42.

(5.2) 61

(5.3) 61

(5.4) 61

(5.5) 61

Table 42: Disturbance Torque Equations Variable Definition

| Variable | Description | Value |
| --- | --- | --- |
| ( | Earth’s gravity constant | 3.986 ( 1014 m3/s2 |
| R | Orbit radius | BOL: 6803 km EOL: 6678 km |
| Iz | Moment of inertia about z axis | 18 kg-m2 |
| Iy | Moment of inertia about y axis | 62 kg-m2 |
| ( | Maximum deviation of z axis from vertical | 2.5° |
| Fs | Solar constant | 1,367 W/m2 |
| c | Speed of light | 3 ( 108 m/s |
| As | Worst case cross-sectional area | 1.2 m2 |
| q | Reflectance factor | 0.6 |
| i | Orbit inclination | 64° |
| cps - cg | Distance from center of solar pressure to center of mass | 0.3 m |
| D | Residual dipole of vehicle | 1 A-m2 |
| B | Earth’s magnetic field | BOL: 5.1 ( 106 T EOL: 5.3 ( 106 T |
| ( | Atmospheric density | BOL: 2.47 ( 10-13 kg/m3 EOL: 1.95 ( 10-11 kg/m3 |
| Cd | Drag coefficient | 2.2 |
| V | Spacecraft velocity | BOL: 7655 m/s EOL: 7726 m/s |
| cpa - cg | Distance from center of aerodynamic pressure to center of mass | 0.2 m |

These disturbance torques are calculated at both BOL and EOL conditions to ensure the inclusion of a worst-case scenario.  These results are shown in Table 43.

Table 43: Disturbance Torque Calculations

| Torque | BOL | EOL |
| --- | --- | --- |
| Gravity-Gradient | 7.2 ( 10-6 N-m | 7.6 ( 10-6 N-m |
| Solar Radiation | 2.6 ( 10-6 N-m | 2.6 ( 10-6 N-m |
| Magnetic Field | 5.1 ( 10-5 N-m | 5.3 ( 10-5 N-m |
| Aerodynamic | 3.8 ( 10-6 N-m | 3.0 ( 10-4 N-m |
| Total Disturbance Torque | 6.4 ( 10-5 N-m | 3.7 ( 10-4 N-m |

### 5.2.4 Attitude Control Components

A three axis stabilized system can include many different attitude control actuators, including thrusters, reaction and momentum wheels, control moment gyroscopes, and magnetic torquers.  For Aiolos, thrusters and gyros are not reasonable solutions due to their high cost and weight.  The best solution appears to be a bias momentum wheel aligned along the pitch axis.  The pitch axis is normal to the orbit plane, and such a wheel allows movement along this axis while stabilizing the other two axes.  Magnetic torquer bars are included to account for attitude drift and to de-saturate the momentum wheel.  The following two equations are used to size the momentum wheel and the magnetic torquers.61

(5.6) 61

(5.7) 61

In the above equations, h is angular momentum, T is the worst-case disturbance torque, P is orbital period, (a is allowable motion, D is electrical current, and B is the Earth’s magnetic field.  These values are calculated and shown in Table 44.

Table 44: Attitude Actuator Calculations

| Parameter | BOL | EOL |
| --- | --- | --- |
| Momentum Storage | 2.1 N-m-s | 11.4 N-m-s |
| Magnetic Torquer Current | 1.7 A-m2 | 9.1 A-m2 |

Ithaco Space Systems produces momentum wheels and magnetic torquers that meet the needs of Aiolos.  Ithaco has experience in building over 150 reaction and momentum wheels that have met the needs of a wide range of missions.4  The particular wheel chosen for Aiolos is an Ithaco TW-16B32.  This momentum wheel provides a momentum capacity of 16.6 N-m-s and a reaction torque of 32 mN-m.4  Figure 60 shows the wheel and Table 45 provides information on this type of wheel.

Figure 60: Ithaco Type A and B Wheels4

Table 45: Ithaco Wheel TW-16B32 Specifications4

| Description | Value |
| --- | --- |
| Speed Range | ( 5100 rpm |
| Momentum Capacity | 16.6 N-m-s |
| Reaction Torque | 32 mN-m |
| Size | 25.5d ( 9.3 cm |
| Mass | 5.9 kg |
| Peak Power | 50 W |
| Steady State Power (1000 rpm) | 6.5 W |

In addition to the wheel, three magnetic torquers are included in Aiolos to provide the ability to control the attitude about all three axes and to de-saturate the momentum wheel.  Ithaco Space Systems also produces magnetic torquers that fit the requirements of Aiolos.  Three TR10CFR torquers are used, each providing a moment of 12 A-m2.  These torquers are shown in Figure 61 and information is provided in Table 46.

Figure 61: Ithaco Magnetic Torquers4

Table 46: Ithaco Magnetic Torquer TR30CFN Specifications4

| Description | Value |
| --- | --- |
| Moment | 12 A-m2 |
| Size | 1.8d ( 38.1 cm |
| Mass | 1 kg |
| Power | 0.9 W |
| Voltage | 15.4 V |

## 5.3 Power

An efficient method of generating, storing, and regulating electric power onboard the spacecraft is crucial to the success of the mission.  The various subsystems are comprised of multiple components, all with their own specific power requirements that must be met by the power system.  The power generation system on Aiolos converts solar energy into useable electric energy, which is used to power the spacecraft in daylight.  The energy storage system powers the spacecraft in eclipse and during peak operating conditions.  A regulation system is employed to monitor power usage among the various components.

### 5.3.1 Operating Conditions and Requirements

As stated previously, the power subsystem is tasked with providing ample power to the various spacecraft subsystems when needed.  Each component of each subsystem has its own power and voltage requirements that must be met for optimal operation.  These requirements vary between what is needed on average and what is needed in a peak condition and are shown in Table 47.

Table 47: Subsystem Power Requirements

| Component | Quantity | Average Power (W) | Peak Power (W) |
| --- | --- | --- | --- |
| Reaction Wheel | 1 | 17 | 50 |
| Torque Rod | 3 | 2.7 | 4.8 |
| Earth Sensor | 2 | 16 | 16 |
| Magnetometer | 1 | 0.1 | 0.1 |
| Sun Sensor | 5 | 0.5 | 0.5 |
| GPS Unit | 1 | 5.5 | 7 |
| Receiver | 1 | 1 | 1 |
| Transmitter | 1 | 0 | 30 |
| Computer | 1 | 5 | 5 |
| Deployment Mechanisms | 2 | 0 | 5 |
| Solar Array Drive Assembly | 2 | 14 | 14 |
| MicroMAPS | 1 | 16.15 | 27.2 |
| Charge Control Unit | 1 | 7 | 7 |
| Totals | 22 | 84.95 | 164.6 |

The power generation system is designed to operate during daylight and is sized using the average power requirements.  The energy storage system is designed to operate during eclipse and also handles the peak power requirements.  In the event that a peak power condition exists during daylight operation, the energy storage system will operate in tandem with the power generation system to provide the necessary power.

### 5.3.2 Power Generation

A power generation system is employed to provide the necessary power to the subsystems during daylight and also to recharge the energy storage system.  Several options are available for accomplishing this task.  Since the photovoltaic method has been in successful use for a number of years, this option will be used for Aiolos.  Solar energy is a bountiful source of power, limited only by the degradation of the solar cells.

The solar cells utilized are the triple-junction gallium arsenide variety manufactured by Spectrolab.56  The solar cell parameters are outlined in Table 48.  The cells are to be combined into a planar array, as opposed to being mounted directly on the body of the spacecraft.  Body mounted cells raise thermal control issues and reduce the efficiency of the cells.  The array is attached to an articulated boom positioned to obtain the best solar incidence angle for maximum power output.

Table 48: Spectrolab Triple Junction Solar Cell Information56

| Parameter | Value |
| --- | --- |
| Area | 28 cm2 |
| Thickness | 191 μm |
| Mass | 2.352 g |
| Voltage | 2.275 V |
| Current | 0.417 A |
| Efficiency (Laboratory) | 26 % |
| Efficiency (Production) | 24.5 % |

The sizing of the array is based on the average power requirements listed in Table 47.  These requirements dictate how much power the array must produce in order to maintain a stable operating environment.  Another important factor is the orbit degradation over the lifetime of the mission.  The solar array power requirement depends on orbital period and therefore is lower at BOL (181 W) than at EOL (189 W).  The array is sized to the larger requirement at EOL and operates with a slight power excess at BOL.  Eq. (5.8) is used to find the solar array power requirement (PSA) where Pe is power required in eclipse, Pd is power required in daylight, Te is time in eclipse, Td is time in daylight, Xe is line efficiency factor in eclipse, and Xd is line efficiency factor in daylight.

(5.8) 61

The actual power production capability of the solar cells is based on the amount of solar radiation received.  The production efficiency listed for these particular triple junction cells is 24.5%.56  Therefore, the ideal power production capability is 335 W/m2, occurring when the incident solar radiation is normal to the surface of the array.  The inherent degradation of the cells (a loss of 23%) must be taken into account to find the actual power production capability at BOL.  The incidence angle of the sun must also be considered, but the array is articulated to achieve a nearly normal incidence angle at all times.  A 10° deviation, however, is assumed to be a worst case scenario, resulting in a BOL power production capability of 254 W/m2.

Over the course of the mission, the array will degrade so that the capability achieved at EOL becomes 250 W/m2.  The power output is based on the lifetime degradation of the cells (0.5 % per year) and the duration of the mission (3 years).61  Using the solar array power requirement and the EOL power production capability, the area of the array is found to be 0.754 m2.  For symmetry purposes, the array area is split between two small arrays with a total mass of 7.25 kg.

The solar array also must provide the proper bus voltage and current, achieved by combining the cells into parallel and series strings.  The cells are combined into parallel strings to produce the bus current, and these strings combine in series to produce the bus voltage.16  Since the entire array is sized according to the conditions at EOL, the individual strings are designed in the same manner.31  A 28 V bus, the nominal value for most spacecraft, is desirable.  Using this value and the solar array power requirement, the bus current is computed at 6.7 A.  The total number of cells in the array (266) is found using the array power requirement and the power production capability per cell at EOL.  The number of cells in parallel (19) is found using the bus current and the current provided per cell at EOL. The number of strings in series (14) is found using the bus voltage and the voltage provided per cell at EOL.

### 5.3.3 Energy Storage

The energy storage system is critical in providing primary power to the spacecraft during eclipse and supplemental power during peak daylight operating conditions.61  The system onboard Aiolos makes use of the cutting edge lithium ion secondary batteries provided by the SAFT Battery Company.32  These higher end batteries save space and mass when compared to nickel cadmium or nickel metal hydride batteries.  Information about the batteries is presented in Table 49.

Table 49: SAFT Lithium Ion Battery Information32

| Parameter | Value |
| --- | --- |
| Specific Energy Density | 125 Wh/kg |
| Voltage | 3.6 V |
| Mass | 1.132 kg |
| Diameter | 0.054 m |
| Height | 0.25 m |
| Thermal Range | 10 – 30 °C |
| Energy Efficiency | 96 % |

The size of the battery pack is based on the spacecraft’s peak power requirements listed in Table 47.  The worst operating condition for the spacecraft is a peak power condition during eclipse.61  Since the solar arrays will not be able to assist in this condition, the batteries must be designed to carry this load.  Normal operation during eclipse will result in an excess of power provided by the battery, subsequently released from the system as thermal energy.

The depth of discharge (DOD), the amount of energy released from the batteries during a discharge period, is also an important factor in determining the battery pack capacity.  A spacecraft operating in LEO experiences about 15 eclipses per day.61  Keeping the DOD low (in this case, 30%) allows the battery to operate nominally until EOL.  The spacecraft will experience 17,000 eclipse cycles, and this DOD level will be maintained because the lithium ion batteries preserve their charge better than other battery choices.

The necessary battery capacity is found to be 385 Wh, which can be achieved using three lithium ion cells in parallel.  The battery must also be able to provide and maintain the bus voltage of 28 V, therefore requiring eight cells in series.  The total pack mass in this configuration is 17.5 kg, compared to a nickel metal hydride pack with 22 cells and a mass of 44 kg.

## 5.4 Command and Data Handling (C&DH)

The primary function of the C&DH subsystem of Aiolos is to store data and to control the functions of the spacecraft.  The data storage requirements include both science and telemetry data.  The C&DH system stores the data until transmission to a ground station.

The C&DH system chosen for Aiolos is the OBC 386 on-board data handling system made by SSTL.48  The processor is an Intel 386EX running the Posix or SCOS operating systems with a 25 MHz clockspeed.  The system has a 128 MB ramdisk and needs a 28 V potential with a 5 W power supply.  No transformer is required since the spacecraft power subsystem provides the same electrical potential from the solar panels.  The system weighs 1.7 kg and dimensions are 330 by 330 by 32 mm.  This system has long flight heritage as it has been used on the following spacecraft: FASAT, TMSat, Tsinghua-1, Tiungsat, and UoSAT-12.

The system serves as a central command unit for spacecraft operations.  The communication subsystem, consisting of the transmitter and receiver, is connected to the C&DH system using two high-speed serial communication channels.  Other subsystems in the spacecraft are connected to the C&DH system via the 10 Mbps Ethernet connection.  The science and telemetry data are stored for later transmission with time flags to differentiate the data.  Interaction between subsystems is also evaluated and controlled by the computer.

## 5.5 Communication

The communication subsystem, made up of a transmitter, a receiver, and an antenna, serves as a link between the spacecraft and the ground station.  Since the configuration of an antenna depends on its frequency range, a single frequency range used for both transmitting and receiving would eliminate the need for having two antennas.  S-band frequency, from 2.0 to 4.0 GHz, offers a good choice for the link frequency.  Since the energy of the signal is proportional to the signal frequency, a higher frequency signal has more energy.  For spacecraft to ground communication S-band technologies have a rich heritage, and many products are available for an S-band communication link.  For these reasons, the S-band frequency is chosen for both uplink and downlink.

### 5.5.1 Antenna

The antenna chosen is the SSTL S-band Quadrifilar Helix Antenna.  The receiving frequency ranges from 2.01 to 2.10 GHz, and the transmitting frequency ranges from 2.22 to 2.29 GHz.  The radiation pattern, shown in Figure 62, is a conical beam with the maximum gain at the radio horizons.

Figure 62: S-band Quadrifilar Helix Antenna Footprint48

The maximum gain configuration of the antenna occurs at each horizon.  Therefore the spacecraft could use the maximum gain opportunity to transmit and receive data as the ground station enters and exits the footprint.  The antenna has a maximum beam width of 120 degrees with no signal strength at nadir.   This beam width translates into a distance of 1472 km from horizon to horizon in a 425 km orbit.  In this orbit, the spacecraft travels at approximately 7.65 km/s, resulting in a total contact duration between the spacecraft and the ground station of about three minutes.  This duration is sufficient due to the data rate of the transmitter and receiver, discussed in the next few paragraphs.  Physically, the antenna is 100 by 100 by 500 mm and has a mass of 0.5 kg.

### 5.5.2 Transmitter

The transmitter chosen for Aiolos is the AeroAstro S-band Transmitter with a transmission range from 2.20 to 2.30 GHz.44  The frequency selected for this mission is 2.25 GHz to counter signal fluctuations and still allow signal transmission.  The maximum output power of the transmitter is 500 mW without an amplifier or a maximum of 5 W with the built-in high power amplifier (HPA).  This extra power comes at a cost as the input power requirement increases from 20 W to 30 W, and the mass increases from 180 g to 500 g with the HPA.  The voltage is set at 28 V to eliminate the need for a transformer.  The transmission rate reaches a maximum at 10 Mbps with the HPA in place and allows a minimum downlink connection time.

MicroMAPS collects 0.45 MB of data per day.  Telemetry data depends on system activity and is estimated as a maximum of 0.45 MB.  Therefore, a maximum of 0.90 MB of data needs to be stored daily.  Since the computer can store up to 128 MB of data, the spacecraft can operate as long as 128 days before requiring an opportunity to transmit.  From LEO, Aiolos will be able to contact a ground station much more often than once every 128 days.  Even in this worst case, the spacecraft would only need two seconds to transmit all of its stored data to the ground station.

### 5.5.3 Receiver

The receiver chosen for Aiolos is the AeroAstro S-band Receiver with a frequency range from 2.025 to 2.120 GHz.44  The frequency is set at 2.060 GHz so that it is at the center of the range.  The data rate which can be received is from 1.0 to 9.6 kbps, and since the uplink data will only be commands, the data will not be more than a KB.  The data rate set for the receiver is 9.6 kbps since this rate allows the maximum amount of data to be received.

The uplink sequence starts when the spacecraft is near the horizon, passing out of the view of the ground station.  At this time, a single signal containing the size of the uplink is received from the ground station.  The computer analyzes the signal to determine when to start the uplink sequence to ensure enough time for the connection.  This process allows the spacecraft to minimize the time required for this connection, since the power of the received signal is strongest at the horizon.  This procedure requires 1 W of power at a 5 V direct current electric potential.  The receiver is 76 by 51 by 25 mm and has a mass of 180 g.

## 5.6 Thermal Management

A thermal management system must be designed to protect Aiolos against radiation from the Sun and the Earth.  These sources are the primary causes of thermal fluctuations within the spacecraft.  Temperatures inside the spacecraft will increase without thermal control components, ultimately disrupting the operation of other subsystems.  These systems will also cease to function properly if the temperature falls dramatically during periods of eclipse.  The following sections show the procedures used to analyze the thermal conditions of the spacecraft and the configuration of the thermal management subsystem.

### 5.6.1 Temperature Limits

The Aiolos thermal subsystem maintains all components within the operating temperature range specified by the manufacturer.  The components include a wide range of temperature limits, listed in Table 50.  Using this data, a specific temperature range is set based on the required operational temperature limits of each component.  The component with the highest minimum temperature determines the lower limit for the spacecraft temperature range, and the lowest maximum temperature determines the upper limit.  Using Table 50, the temperature ranges from 0°C to 30°C.

Table 50: Operational Temperature Limit

| Component | Min. Temp (°C) | Max. Temp (°C) |
| --- | --- | --- |
| MicroMAPS Instrument | -6.67 | 48.9 |
| Ithaco Reaction Wheel | -55 | 70 |
| Ithaco Magnetic Torquer Rods | -34 | 71 |
| Ithaco 3-Axis Magnetometer | -20 | 60 |
| Surrey 2-Axis Sun Sensor | -90 | 90 |
| Computer/Processor | -5 | 50 |
| SSTL S-Band Transmitter | -20 | 50 |
| AeroAstro S-Band Receiver | -40 | 60 |
| SAFT Lithium Ion Batteries | 0 | 30 |
| Aluminum 7075-T73 | N/A | 532 |
| Aluminized Kapton® (MLI) | -269 | 400 |

### 5.6.2 Heat Sources

Two main sources of heat affect Aiolos in LEO: external sources in the environment and internal heat generated by the subsystems.  The external sources include radiation from the Sun and the Earth.  In LEO, the radiation received by Aiolos is approximately equal to the amount of radiation received by the Earth.  Solar flux oscillates during the year based on the Earth’s orientation with respect to the Sun.  An average value of 1353 W/m2 for the solar flux is used in the subsequent analysis.23  The radiation emitted from the Earth must also be considered, and based on an orbital inclination of 64°, the Earth emitted radiation ranges from 220 W/m2 to 246 W/m2.23  A third component of external radiation, Earth-reflected solar flux, is called the albedo.  Based on the orbital inclination, the albedo is 36% of the radiation emitted from Earth.23  Table 51 shows the environmental fluxes in space.

Table 51: Environmental Fluxes in Space23

| Source | Cold (W/m2) | Hot (W/m2) |
| --- | --- | --- |
| Solar | 0 | 1353 |
| Earth Emitted | 220 | 246 |
| Albedo | 28% | 36% |
| Total | 281.6 | 1687 |

The second main source of heating is the internal heat generated by all the subsystems.  Since some components do not use all of the provided power for operation, power is dissipated as heat to prevent overheating.  Power dissipation is listed in Table 52 and totals 39 W for non-active situations and 72 W for active situations.

Table 52: Internal Power Dissipation

| Component | Non-Active (W) | Active (W) |
| --- | --- | --- |
| MicroMAPS Instrument | 6.48 | 10.88 |
| Ithaco Reaction Wheel | 6.8 | 20 |
| Ithaco Magnetic Torquer Rod | 1.08 | 1.92 |
| Ithaco Conical Earth Sensor | 6.4 | 6.4 |
| Ithaco 3-Axis Magnetometer | 0.04 | 0.04 |
| Surrey 2-Axis Sun Sensor | 0.2 | 0.2 |
| GPS Unit | 2.2 | 2.8 |
| Computer/Processor | 2.0 | 2.0 |
| SSTL S-Band Transmitter | 0 | 12 |
| AeroAstro S-Band Receiver | 0.4 | 0.4 |
| SAFT Lithium Ion Battery | 2.4 | 2.4 |
| Battery Charge Control Unit | 2.8 | 2.8 |
| Total | 39.26 | 71.98 |

### 5.6.3 Radiator

The Aiolos thermal management subsystem, which includes radiators and multi-layered insulation (MLI), is designed to be passive to maximize simplicity and minimize cost.  The aluminum structure of the spacecraft is employed to radiate heat.  The radiating surfaces are coated with barium sulfate, a white paint with a low absorptivity (), and a high emissivity ().23  Four radiating surfaces are arranged on two opposing side panels of the hexagonal cylinder.  This configuration allows radiation to be emitted at all times since at least one side of the spacecraft always faces away from the sun.  The following equations for internal heat (Qint), direct solar heat (Qds), Earth reflected heat (Qer), and Earth emitted heat (Qet) are used in conjunction with the variables defined in Table 53.  The spacecraft thermal environment faces four possible scenarios, encompassing active and non-active component operational modes during both daylight and eclipse conditions.  Using the barium sulfate coating, a radiator area of 0.11 m2 meets the requirements of these four operating scenarios.

(5.9)42

(5.10)42

(5.11)42

(5.12)42

(5.13)42

(5.14)42

Table 53: Thermal Calculation Variables and Definitions

| Variable | Description | Value |
| --- | --- | --- |
|  | Emissivity of coating | 0.88 |
|  | Absorptivity of coating | 0.06 |
| a | Albedo | 0.36 |
| PAS | Projected Area normal to Sun | 0.215 m2 |
| A | Area | 0.11 m2 |
|  | Stefan-Boltzmann Constant | 5.67*10-8 W/m2K4 |
| Fsc,sp | Fraction of orbit faces sun | 0.65 |
| Fet | Configuration Factor of Earth | 0.8 |
| Het | Earth constant | 216.48 W/m2 |
| Hds | Average Solar Flux | 1353 W/m2 |
| k | Thermal conductivity | 153 W/mK |

### 5.6.4 Multi-Layered Insulation

Multi-layered insulation prevents radiation damage from both the Sun and the Earth and usually consists of three to thirty layers of insulation material.23  Aiolos uses 20 layers which include inner and outer layers of Kapton surrounding 18 middle layers of Mylar.  The aluminized Kapton is 50 m thick and coated with indium oxide coating, providing a tougher surface than Mylar.  The aluminized Kapton layer has an  of 0.39 and  of 0.75.  Normally would deteriorate to 0.55 at the end of a three year mission, but the coating decreases this rate so that an  of 0.47 is achieved at EOL.23  The inner 18 layers are Mylar film with aluminum backing.  Each layer is 12.5 m thick and has an  of 0.15 and  of 0.34.

Nineteen layers of Dacron netting of thickness 50m prevent the insulation layers from contacting each other.  Made of non-conductive materials, separation layers do not allow conduction heat transfer between the MLI layers.  Small perforations in the layers allow trapped air to escape as the pressure changes during launch.  The blankets are stitched together around the edges and are attached to the spacecraft using Velcro strips.23  Holes are cut in the insulation to accommodate the radiators, the antenna, the MicroMAPS optics, and the solar array drive.

## 5.7 Launch Vehicle

The orbit design discussed previously heavily influences the launch vehicle selection.  Since this project is a NASA mission, launch vehicle selection is restricted to United States vehicles and launch sites.  In addition, the orbit design requires that the launch vehicle reach LEO.  This requirement eliminates vehicles that primarily launch geosynchronous transfer orbit (GTO) missions such as Atlas, Delta III and IV, Sea Launch, and Titan IV.  Launching into a high inclination orbit requires the use of launch sites at either Vandenberg Air Force Base (VAFB) or the Kodiak Launch Complex (KLC).  Due to the size of Aiolos, mass and payload restrictions are not driving factors in the launch vehicle selection.  Structural requirements are considered in Section 5.8.  The most feasible launch vehicles are cheap and reliable and can accommodate the spacecraft as a secondary payload.

Launching as a secondary payload has several implications for the Aiolos mission.  The desired orbital inclination and altitude may not be attainable, depending on launch vehicle availability.  This design assumes that the launch vehicle can reach the optimal orbit discussed previously.  Aiolos is designed to launch on several vehicles to improve the number of launch opportunities and to provide competition for the launch contract.

### 5.7.1 Cost Comparison

Launch costs make up a significant portion of the cost of space missions and therefore is used to determine the launch vehicle alternatives.  As a secondary payload, one way to estimate the cost of a particular vehicle is by comparing costs per mass to a particular orbit.  Since a secondary payload only pays a fraction of the total launch vehicle price, this analysis is intended to provide a better comparison between launch vehicle options.  Table 54 shows these values for the most commonly used vehicles.

Table 54: Launch Vehicle Cost Analysis61

| Launch Vehicle | Cost per kg to LEO (FY00$K/kg) |
| --- | --- |
| Athena I | 22.5 |
| Athena II | 13.3 |
| Delta II (7920) | 9.8 – 10.8 |
| Pegasus XL | 28.3 |
| Space Shuttle | 16.4 |
| Titan II | 19.4 |
| Taurus | 14.3 – 15.7 |

Based on the cost comparison, three vehicles are selected for the Aiolos spacecraft: Athena II, Delta II, and Taurus.  These three provide the lowest cost per mass and conveniently, they have three different launch service providers: Lockheed Martin, Boeing, and Orbital Sciences, respectively.  This fact should help lower the mission cost due to the competition between the companies.

### 5.7.2 Athena II

Lockheed Martin Astronautics produces the Athena II launch vehicle (Figure 63).  The Athena II is a four-stage vehicle made up of three solid motors and a small liquid injection stage.28  The first launch of Athena II occurred in 1998, and the Athena family has flown at a rate of 0-2 per year because of relatively low demand.28  Lockheed Martin reports that a flight rate of at least 10 per year is possible.28  Launch operations from Kodiak Launch Complex in Alaska provide a mission inclination range from 64-116°.28  Based on Figure 64, Athena II can carry about 1650 kg to an orbit of 425 km.  The payload fairing dimensions are shown in Figure 65.

Figure 63: Athena II Launch Vehicle3

Figure 64 Athena II Performance28

Figure 65: Athena II Payload Fairing28

### 5.7.3 Delta II

Boeing Expendable Launch Services produces the Delta family of launch vehicles (Figure 66).  Two stage Delta II vehicles typically launch into LEO.15  The 7920 model (Figure 67), the most cost effective version, uses nine strap-on motors and two stages to reach mission orbit.28  The Delta II 7920 configuration has been in operation since 1990, and Delta II vehicles have demonstrated a peak flight rate of 12 per year.28  A launch site at Vandenberg Air Force Base provides a range of orbital inclinations: 63-145°.28  The expected performance of the vehicle (4000 kg to 425 km orbit) is shown in Figure 68 and the payload fairing dimensions are shown in Figure 69.

Figure 66: Delta II Launch Vehicle Family15

Figure 67: Delta II Launch Vehicle15

Figure 68: Delta II 7920 Performance28

Figure 69: Delta II Payload Fairings15

### 5.7.4 Taurus

An Orbital Sciences Corporation launch vehicle, the Taurus is a ground-launched derivative of the Pegasus launch vehicle first launched in 1998 (Figure 70 and Figure 71).28  The two basic configurations are the SSLV (Standard Small Launch Vehicle) that uses the Peacekeeper first stage and the Commercial that uses the Castor 120 first stage motor.28  The SSLV Taurus is only available for U.S. government payloads because of the use of the surplus missile stage.28  The launch site at Vandenberg Air Force Base allows launches to orbital inclinations of 60-120°.28  As shown in Figure 72, the Taurus 2110 (smaller payload fairing) can carry a payload of 1050 kg to an orbit of 425 km.  The comparison of the payload fairings is shown in Figure 73.

Figure 70: Taurus Launch Vehicle Family30

Figure 71: Taurus Launch Vehicle30

Figure 72: Taurus Performance28

Figure 73: Taurus Payload Fairing30

### 5.7.5 Comparison of Options

Aiolos is designed so that it can launch in all three launch vehicle options: Athena II, Delta II 7920, and Taurus.  A listing of parameters relevant to this design is provided in Table 55.

Table 55: Launch Vehicle Selection Criteria3,15,28,30

| Vehicle | Athena II | Delta II 7920 | Taurus |
| --- | --- | --- | --- |
| Launch Service Provider | Lockheed Martin | Boeing | Orbital Sciences |
| Launch Site (for 64°) | KLC | VAFB | VAFB |
| Unit Cost ($M) | 26 | 50-55 | 20-22 |
| Cost per kg to LEO ($K/kg) | 13.3 | 9.8-10.8 | 14.3-15.7 |
| Flight Record | 3/5 | 103/105 | 5/6 |
| Flight Rate (units per year) | 0-2 | 10-12 | 0-2 |
| Payload (to 450 km, 64°) | 1650 kg | 4000 kg | 1050 kg |
| Orbit Injection Accuracy | ± 20 km | ± 9.3 km | ± 29.6 km |
| Payload Fairing | 6.1 ( 2.3 m | 8.49 ( 2.9 m | 5.5 ( 1.6 m |
| Axial Load | 8.0 g | 6.0 g | 8 g |
| Lateral Load | 1.8 g | 2.5 g | 2.5 g |
| Min Longitudinal Frequency | 30 Hz | 35 Hz | 25 Hz |
| Min Lateral Frequency | 12 Hz | 15 Hz | 25 Hz |

Although Aiolos is designed to launch in all three vehicles, a need exists to rank the vehicles based on preference.  Several parameters are most important to this decision: cost, launch environment, reliability, availability, mass to orbit, and payload volume.  Cost is explained previously and is still a factor in the comparison.  Launch environment describes the forces and vibrations the spacecraft will encounter during launch.  Reliability describes the chance of launch vehicle failure, and availability describes the number of opportunities to launch.  In all cases, Aiolos is well within mass to orbit and payload volume restrictions, but large values allow more capability for other missions sharing the particular vehicle.  For each vehicle, these values are analyzed qualitatively, and Table 56 provides the ranking of each of these parameters, with a value of one being the best case.  Using this analysis, Delta II 7920 is the preferred launch vehicle.

Table 56: Ranking of Launch Vehicles

| Vehicle | Athena II | Delta II 7920 | Taurus |
| --- | --- | --- | --- |
| Cost | 2 | 1 | 3 |
| Launch Environment | 2 | 1 | 3 |
| Reliability | 3 | 1 | 2 |
| Availability | 2.5 | 1 | 2.5 |
| Mass to Orbit | 2 | 1 | 3 |
| Payload Volume | 3 | 1 | 2 |

## 5.8 Structures

The structural design adheres to the constraints set forth by the three launch vehicles: Athena II, Delta II, and Taurus.  The initial designs included the use of titanium but were revealed to be cost inefficient.  The final design consists of two decks of equal length, made entirely with Aluminum 7075-T73 plates, and a wall thickness of 15.075 mm.  The structural analysis begins with the material properties and concludes with the final structural design based on the launch constraints.  The material properties for Aluminum 7075-T73 are summarized in Table 57.  The equations following the table are used to find the forces, loads, and minimum thickness as constrained by each launch vehicle.

Table 57: Aluminum 7075-T73 Material Properties

| Material Properties | Values | Units |
| --- | --- | --- |
| Coefficient of Thermal Expansion, AL | 24 | (106 K)-1 |
| Ultimate Tensile Strength, ult | 460 × 106 | N/m2 |
| Yield Strength, ys | 390 × 106 | N/m2 |
| Young’s Modulus, EAL | 10.3 × 106 | Psi |
| Percent Elongation, eAL | 0.08 | % |
| Ductility | 0.1 |  |
| Fracture Toughness, KALIC | 20 × 106 | Pa m0.5 |
| Melting Temperature, Tmelt | 890 | K |
| Specific Heat, cAL | 0 |  |
| Thermal Conductivity, kAL | 150 | W m-1 K-1 |
| Modulus of Elasticity, GAL | 3.9 × 106 | Psi |
| Poisson’s Ratio, AL | 0.321 |  |
| Cost | 1430 | US$/tonne |

(5.15)61

(5.16)61

(5.17)61

(5.18)61

(5.19)61

(5.20)61

(5.21)61

(5.22)61

The previous equations use the following variables: W, the weight load of the empty structure; PLimit,axial and PLimit,lateral, the respective axial and lateral limit loads for launch; Peq, the equivalent force; Pult, the ultimate force; R, the moment arm taken to be half of the structure length; M, the moment primarily due to lateral launch loads; ult, the ultimate stress; L, the length of the structure; k, the spring constant for a fixed-fixed configuration; AL, Poisson’s ratio for aluminum; and EAL, Young’s Modulus for aluminum.  Calculated values for the three launch vehicles are shown in Table 58.

Table 58: Launch Vehicle Structural Impact

| Load Limits | Athena II | Delta II | Taurus |
| --- | --- | --- | --- |
| Paxial (kN) | 10.3 | 8.59 | 10.3 |
| Plateral (kN) | 2.33 | 3.23 | 3.23 |
| M (kJ) | 1.42 | 1.97 | 1.97 |
| Peq (kN) | 15.0 | 15.1 | 3.87 |
| Pult (kN) | 22.5 | 22.6 | 5.81 |
| tmin (mm) | 0.123 | 0.124 | 0.032 |
| tbuckling (mm) | 7.82 | 7.83 | 5.58 |

In addition to the static analysis, a dynamic analysis must be performed to ensure the vibrations of launch are within the constraints of the MicroMAPS operating restrictions.  Calculations are made for natural frequencies (f), deflections (), and spring constants (k) for a uniformly loaded beam.  In the equations below, Aside is the cross-sectional area of the side view, mtotal is the total mass of the structure, g is the acceleration due to gravity, and  is the area moment of inertia with respect to the x-axis about the center of gravity.  Results are shown in Table 59.

(5.23)61

(5.24)61

(5.25)61

(5.26)61

(5.27)61

Table 59: Launch Vehicle Dynamic Impact

| Dynamic Analysis | Athena II | Delta II | Taurus |
| --- | --- | --- | --- |
| faxial (Hz) | 4870 | 4870 | 4870 |
| axial (µm) | 0.103 | 0.0859 | 0.103 |
| kaxial (kg/s2) | 1.25 × 1010 | 1.503 × 1010 | 1.25 × 1010 |
| flateral (Hz) | 2790 | 2790 | 2790 |
| lateral (µm) | 0.0888 | 0.123 | 0.123 |
| klateral (kg/s2) | 1.45 × 1010 | 1.05 × 1010 | 1.05 × 1010 |

An initial structural model can be designed once the launch constraints have been calculated.  Table 60 provides the mass of each subsystem and the total for Aiolos.

Table 60: Subsystem Mass Summation

| Subsystem Section | Mass (kg) |
| --- | --- |
| ADCS | 16.6 |
| C&DH | 1.70 |
| Communication | 1.18 |
| Orbit Determination | 1.00 |
| Power | 25.9 |
| Thermal | 4.25 |
| MicroMAPS | 6.40 |
| Subsystems Total | 57.0 |
| Empty Structure | 74.7 |
| Aiolos Total | 132 |

The dimensions of Aiolos are optimally designed to accommodate MicroMAPS within a hexagonal cylinder.  One deck of the Aiolos design has a height of 406 mm, a face width of 264 mm, and an edge width of 610 mm, with a wall thickness of 15.9 mm, ceiling thickness of 6.35 mm, and a thermal insulation thickness of 15.9 mm.  Figure 74 shows MicroMAPS within Aiolos for a visual scale interpretation.

Figure 74: MicroMAPS Location within Aiolos

Subsystems are individually added at specific locations in the structure to minimize the mass and area moments of inertia values.  The resulting design is shown in Figure 75.

Figure 75: Complete Aiolos Configuration

The ADCS subsystem is highlighted in red, power is in green, C&DH is in dark blue, communication is in teal, and MicroMAPS is in purple.  The total mass and area moments of inertia are calculated in Table 61.

Table 61: Inertia Calculations

| Moments of Inertia | Values | Units |
| --- | --- | --- |
|  | 0.0128 | m4 |
|  | 0.0223 | m4 |
|  | 0.0267 | m4 |
|  | 53.1 | kg m2 |
|  | 61.6 | kg m2 |
|  | 18.0 | kg m2 |

## 5.9 Cost Analysis

A preliminary cost estimation is calculated for the spacecraft using a parametric cost analysis method.61  The result is a theoretical first unit (TFU) cost in thousands of fiscal year 2003 dollars.  Cost estimations for each subsystem are based on the corresponding mass parameter.  The total production cost of the spacecraft is the summation of the individual subsystem costs.  The cost analysis result is shown in Table 62.

Table 62: Cost Analysis

| Subsystem | Mass Parameter (kg) | TFU Cost ($K FY 03) |
| --- | --- | --- |
| Communication | 1.18 | 174 |
| Structure | 74.7 | 1030 |
| Thermal | 4.25 | 148 |
| Power | 25.9 | 1410 |
| C&DH | 1.70 | 903 |
| ADCS | 6.93 | 1390 |
| Total |  | 5060 |

## 5.10 Spacecraft Summary

Aiolos is a functional platform for achieving the MicroMAPS science goals as stated by the customer.  A three-year lifetime allows for an adequate understanding of the carbon monoxide transport processes in the Earth’s troposphere.  Knowledge of how these processes vary over time and on a global scale is also gained.  The supporting subsystems are designed to meet the performance goals at a reasonable cost.

# References

- “Alaska Aerospace Development Corporation’s Kodiak Launch Complex."  Space Today Online.  8 November 2002.  http://www.spacetoday.org/Rockets/Spaceports/KodiakIsland.html.

- Asato, D.  Propulsion Branch.  Guidance, Navigation, and Control Division.  NASA Goddard Space Flight Center.  Electronic Mail Correspondence.  14 January 2003.

- “Athena.”  Lockheed Martin Company.  22 March 2003. http://www.lockheedmartin.com/factsheets/product384.html

- “Attitude Control Products.”  Ithaco Space Systems.  29 March 2003. http://www.ithaco.com/products.html.

- Bergquist, A., et al.  “Proposed Design for VASCAT.”  Design Report.  Aerospace and Ocean Engineering, Virginia Tech.  Blacksburg, VA.  Spring 2002.

- Bertin, J. J., and M. L. Smith.  Aerodynamics for Engineers.  Third Edition.  Upper Saddle River, New Jersey: Prentice Hall, 1998.

- Bray, B. "Staying Cool on the Space Station".  NASA Marshall Space
Flight Center.  Huntsville, AL. 14 Oct 2002.  http://liftoff.msfc.nasa.gov/avantgo/stage/news%2Dstationcool.asp.

- “CB Series 28Vin DC / DC Converters.” Martek Power Abbot, Inc. 2003. http://www.martekpowerabbott.com.

- Cengel, Y. A.  Introduction to Thermodynamics and Heat Transfer.  The McGraw-Hill Companies, Boston, MA, 1998.

- Companion, J. A.  Virginia Space Grant Consortium.  Electronic Mail Correspondence.  October 2002 –May 2003.

- “Clark.”  JPL Mission and Spacecraft Library Quicklook.  20 September 2002. http://samadhi.jpl.nasa.gov/msl/QuickLooks/clarkQL.html.

- Connors, V., Larar, A., Beck, S., and Smith, W., “Proteus Payload.”  NASA Goddard Spaceflight Center.  Greenbelt, MD.  12-14 May 1999.  http://eospso.gsfc.nasa.gov/eos_homepage/SAFARI/workshop_links/ptslarar.pdf.

- Connors, V.  NASA Langley Research Center.  Informal Conversation.  Blacksburg, VA.  11 February 2003.

- Dallas Semiconductor.  1 March 2003.  http://www.dalsemi.com

- “Delta.”  The Boeing Company.  22 March 2003.  http://www.boeing.com/defense-space/space/delta/flash.html.

- “Designing a Spacecraft Power System.”  Hall, C. D.  20 March 2003.  http://www.aoe.vt.edu/~chall/courses/aoe4065/.

- Digi-Key Corporation.  April 20, 2003.  http://www.digikey.com.

- Doody, D.  Basics of Space Flight.  Jet Propulsion Laboratory.  Pasadena, CA.  February 2001.  Available: http://www.jpl.nasa.gov/basics/.

- “Eclipse Aviation Terminates Contract with Williams International.”  Eclipse Aviation.  13 April 2003.  http://www.eclipseaviation.com.

- “engApplets.”  W. Davenport, R. Kapania, K. Rojiani, K. Singh, Virginia Tech.  25 April 2003.  http://www.engapplets.vt.edu/.

- Emerson and Cuming.  April 22 2003.  http://www.emersoncuming.com.

- Etkin, B., and Reid, L. D.  Dynamics of Flight – Stability and Control.  Third Edition.  New York: John Wiley & Sons, Inc., 1996.

- Gilmore, D.G. and Bello, M., (editors).  Satellite Thermal Control Handbook.  The Aerospace Corporation Press, El Segundo, CA, 1994.

- Hall, C. D.  “Request for Proposal: Air and Space Opportunities for the MicroMAPS Instrument.”  20 September 2002.  http://www.aoe.vt.edu/~chall/courses/aoe4065/RFPMicroMAPS.pdf.

- Holman, J.P.  Heat Transfer.  The McGraw-Hill Companies: New York, NY, 1996.

- Humble, R.W., G. N. Henry, and W. J. Larson.  Space Propulsion Analysis and Design.  The McGraw-Hill Companies, 1995.

- Hwang, Y.  “Attitude Determination Using GPS.”  1 November 2002.  http://www-ccar.colorado.edu/~hwangy/gps_atti.htm.

- Isakowitz, S. J., J. P. Hopkins, and J. B. Hopkins.  International Reference Guide to Space Launch Systems.  Third Edition.  American Institute of Aeronautics and Astronautics, Reston, VA, 1999.

- Kutz, M.  Temperature Control.  John Wiley & Sons, Inc., New York, NY, 1968.

- “Launch Vehicle Systems.”  Orbital Sciences Corporation.  Dulles, VA.  8 November 2002. http://www.orbital.com/LaunchVehicle/.

- Lennox, S.  Department of Aerospace and Ocean Engineering.  Informal Conversation.  Blacksburg, VA.  27 March 2003.

- “Lithium Ion Batteries.”  SAFT Battery Company.  Saft Poitiers, France.  17 March 2002.  http://www.saftbatteries.com/130-Catalogue/PDF/space_lithium.pdf.

- Marchman, J. F.  Introductory Aircraft Design.  Second Edition.  Blacksburg, VA: A-1 Copies, 2001.

- “MicroMAPS- A Low Cost Orbital Remote Sensor for the Detection of CO and N2O.”  Resonance Ltd.  Barrie, Ontario.  31 October 2002.  http://www.resonance.on.ca/mmaps.html.

- Midon Design.  1 April 2003.  http://www.midondesign.com

- Moreau, M. C.  Flight Dynamics Analysis Branch.  Guidance, Navigation, and Control Division.  NASA Goddard Space Flight Center.  Electronic Mail Correspondence.  November 2002.

- Morrow, B.  Resonance Ltd.  Electronic Mail Correspondence.  November 2002.

- “NASA ERAST – A Gateway into Future Aeronautics.”  NASA.  2 November 2001.  http://www.dfrc.nasa.gov/Projects/Erast/erast.html.

- “NASA Facts.”  NASA – Dryden Flight Research Center.  15 April 2003.  http://www.dfrc.nasa.gov/Newsroom/FactSheets/index.html.

- “NASA Terminates Clark Science Mission.”  NASA Headquarters Press Release 98-35.  Washington, DC.  25 February 1998.  http://geo.arc.nasa.gov/sge/landsat/clark.html.

- “NB Series 28Vin DC / DC Converters.” Martek Power Abbot, Inc. 2003. http://www.martekpowerabbott.com

- Pisacane, V, L. and Moore, R. C. (editors).  Fundamentals of Space Systems.  Oxford University Press, New York, NY, 1994.

- Point Six, Inc.  10 April 2003.  http://www.poinsix.com/cgi-bin/PointSix.cgi?1-Wire

- “Products and Services.”  AeroAstro Inc.  Ashburn, VA.  8 April 2003. http://www.aeroastro.com/products.html.

- Raymer, D. P., ed.  Aircraft Design: A Conceptual Approach.  Third Edition.  Reston, Virginia: American Institute of Aeronautics and Astronautics, Inc., 1999.

- Rummell, K. and Walberg, G.  “Small Spacecraft Technology Initiative: Measurement of Air Pollution from Satellites (MicroMAPS) Instrument Interface Control Document.”  SSTI-SEIT-014.  NASA Contract NASW-4944.  5 May 1995.

- “SAFT-Space Industry.”  SAFT Battery Company.  Saft Poitiers, France.  9 November 2002.  http://www.saftbatteries.com/space_industry/index.htm.

- “Satellites and Services.”  Surrey Satellite Technology Ltd.  22 March 2003. http://www.sstl.co.uk/services/subpage_services.html.

- “Scaled Composites Unveils Proteus, A New High-Altitude, Multi-Mission Aircraft.”  Scaled Composites.  Mojave, CA.  Updated 23 September 1998.  http://www.scaled.com/projects/proteus/proteus.htm.

- Schetz, J. A.  Boundary Layer Analysis.  Upper Saddle, New Jersey: Prentice Hall, 1993.

- “Software for Aerodynamics and Aircraft Design.”  W. H. Mason, Virginia Tech.  15 March 2003.  http://www.aoe.vt.edu/~mason/Mason_f/MRsoft.html.

- “Solar Cells.”  Spectrolab, A Boeing Company.  Sylmar, CA.  10 November 2002.  http://www.spectrolab.com/prd/prd.asp.

- Sze, N., Anthropogenic CO emissions: Implications for the atmospheric CO-OH-CH4 cycle, Science, 195673-674 1977.

- “Tornado: A Vortex lattice MATLAB Implementation for 
Linear Aerodynamic Wing Applications.”  T. Melin, Royal Institute of Technology KTH, Sweden.  17 February 2003.  http://www.flyg.kth.se/divisions/aero/software/tornado.

- Tri-M Systems and Engineering.  22 February 2003.  http://www.tri-m.com

- “Triple Junction Solar Cells.”  Spectrolab, A Boeing Company.  Sylmar, CA.  13 March 2003.  http://www.spectrolab.com/DataSheets/TJCell/tj.pdf.

- “UIUC Airfoil Data Site.”  M. Selig, University of Illinois at Urbana-Champaign.  18 March 2003.  http://www.aae.uiuc.edu/m-selig/ads.html.

- U.S. Composite.  22 March 2003.  http://www.shopmaninc.com/crbonpage.html.

- Walberg, G., H. G. Reichle, and W. H. Morrow.  “Design and Testing of the MicroMAPS Gas Filter Correlation Radiometer.”  Final Report SSTI:94C:004.  21 January 1999.

- “Website for the Defense Industries – Airforce.”  Airforce Technology.  http://www.airforce-technology.com/index.html.

- Wertz, J. R. and Larson, W. J., (editors).  Space Mission Analysis and Design.  Third Edition.  Microcosm Press and Kluwer Academic Publishers, Boston, 1999.

- Williams International.  1 April 2003.  http://www.williams-int.com/index.htm.

- “World Population Density.”  McGraw-Hill Online Learning Center.  22 March 2003. http://highered.mcgraw-hill.com/sites/007248179x/student_view0/chapter8/

web_map_4.html.

# Footnotes

* Please note that the RFP was altered after a February 2003 meeting with Dr. Vickie Connors.  The old requirements are enclosed in brackets.

* If the customer desires a turboprop power plant, one could be installed without extensive modifications to the airframe.

# Text boxes

1800 lb fuel

Zero Fuel

Empty weight

Gust

Maneuver