SOHO OPERATIONAL SCRIPT

Maneuver End

(SOHO Server/SCRIPTS/GENERIC SCRIPTS/Mnvr End Script)

Version 16.0

Based on:	CR #G1314, Gyroless User’s Manual:  RMW_TO_NM_GYROLESS

Change Record:

1.	13 Oct 98 - Changed script to account for only using IRU B, OCD 972.

2.	25 Feb 99 - Deleted IRU B operations from script, SCRF 1108.

3.	28 Feb 99 - Added enabling of the free process after transitioning to normal mode.  Added line numbers.  Added FDF activities, SCRF 1108.

4.	10 May 99 - Added step for FOT to recover MDI per OCD 1177 (CR 1186, MOCR 99-0261) NJP

5.0	9 Jun 99 - Added step to close LV A and set ACU patch 5 staircase filter threshold to 600 (MOCR 99-0304, CR 1229, OCD 1193) NJP

5.1	10 Jun 99 - Added cmds to disable corrective actions for std mon channels 24,25,31-34 after LV A is closed.  NJP

6.0	21 Jul 99 - Updated script per Gyroless User’s Manual.  Deleted commanding for COBS free process and SSU SEU standard monitoring.  Deleted closing of latch valve A and switch off of cat bed heaters A.  Deleted star magnitude threshold commanding (CR G1314, MOCR 99-0413) HWB

6.1	17 Aug 99 - Added star eligibility commanding and starting experiment off-pointing monitoring function.  HWB

6.2	8 Sep 99 – Changed a_roll_trim to a_prof_rmw_nm in step 3.  Reversed order of profile and roll telemetry update in step 3.  Added line to zero the guide star RSL offset and recalculate RSL offset for other tracked stars in step 5.  Added note to indicate when to use restricted search track in step 5.  Added note to notify SOC NRT is available after completion of SVM activities.

6.3	24 Sep 99 – Moved closing MDI ISS loop to after enabling experiment offpointing monitoring.  Added comments to clarify choice of uplinking new RSL or using the current RSL.  HWB

7.0	22 Oct 99 – Added TSTOL procedures a_crs_drft_est and a_crs_drft_upd after RSL activity.  CR 1393  HWB

8.0	3 Oct 01 - Deleted procedures a_rolltm_set and a_r_offz, leaving them to be called by a_r_str_en.  Also, deleted procedures k_cdmu_mem_sp, k_cdmu_mem_sa.  CR 1690, MOCR 01-0140.  NJP

9.0	11 Jul 06 - Added line to switch back to nominal limits for SWAN before running n_fl_llockout.  Also, added note to inform FDF of final positions of newly tracked stars.  OCD#2135, CR #2170, MOCR#06-0106.  NJP

10.0	20 Sep 06 - Skip SWAN recovery actions if only a roll maneuver was performed. OCD#2150, CR#2228, MOCR#06-0124.  NJP

11.0	20 Dec 06 - Added new SWAN recovery procedure n_fl_manrec. OCD#2184, CR#2237, MOCR#06-0142.  NJP

12.0	2 May 07 - Added new procedure k_rwslupd_ena, added procedure and criteria to enable ESR warning flag for CDS, and removed obsolete trending request. OCDs#2233, 2234, CR#2258, MOCR#07-0024.  NJP

13.0	24 Sep 07 - Removed ESR warning flag enable for SWAN, added line to send CELIAS recovery load at SOC/CELIAS direction. OCDs#2259, 2260, CR#2297, MOCR#07-0094.  NJP

13.1	28 Sep 07 – Made additional comment changes for SWAN recovery and resumption of normal operations.  HWB

14.0	28 May 08 – Changed to a 3 minute WAIT between taking SWAN out of launch lock position and starting nominal SWAN observations.  Added c_fl_opendoors before k_set_esrwarn.  (OCDs#2295, 2317, CR#2378, MOCR#08-0016) NJP

15.0	20 Nov 08 – Added note to wait for SOC direction and ensure approximately 24 hrs since burn completion before running CDS door open procedure.  Also, eliminated CDS ESR warning flag enable. (OCDs#2332, 2343, CR#2524, MOCR#08-0188) NJP

16.0	2 Apr 10 – Made changes as requested by experiment teams for bogart mission phase. (OCD#2457, CR#2636, MOCR#10-0028) NJP

Prerequisites:

1.	AOCS in RMW

2.	FCV A OFF

3.	Thruster monitoring disabled

4.	Roll attitude known

5.	Cat bed A heaters OFF

6.	LVA CLOSED

Loads:

RSL_TBL_YYDDD

Main Activities:

1.	Acquire new guide star

2.	Trim roll attitude

3.	Transition to NM

4.	Enable roll steering law

5.	Post maneuver configuration

6.	Instrument restoral

Plots Required:

FDF Activities:

Provide RSL table

|  | Pos | Activity C’est du gateau | Procedure |
| --- | --- | --- | --- |
| 1 | FOT | Bring up command panel for Maneuver End, if available. | MAN_END_YYDDD |
| 2 |  | STEP 1: ACQUIRE NEW GUIDE STAR |  |
| 3 |  | Acquire new star (as required) | a_new_star |
| 4 |  |  |  |
| 5 |  | STEP 2: TRIM ROLL ATTITUDE |  |
| 6 |  | Adjust roll attitude to RSL position | a_prof_rmw_nm |
| 7 |  |  |  |
| 8 |  |  |  |
| 9 |  | STEP 3: TRANSITION FROM RMW TO NM |  |
| 10 |  | Transition from RMW to NM | a_rmw_nm |
| 11 |  |  |  |
| 12 |  |  |  |
| 13 |  |  |  |
| 14 |  |  |  |
| 15 |  |  |  |
| 16 |  | STEP 4: ENABLE ROLL STEERING LAW |  |
| 17 |  | Uplink new roll steering law LOAD NAME: RSL_TBL_YYDDD OR Reset roll steering law in ACU if current RSL table is valid | a_r_str_set OR a_r_str_rst |
| 18 |  | Enable roll steering law function and reset ACU memory dump location. - Zero guide star RSL offset and recalculate RSL offset for other tracked stars. - Set up roll attitude telemetry for SSU based operations. | a_r_str_en Calls: a_r_offz a_rolltm_set |
| 19 |  | Enable automatic calculation of CRS drift | a_crs_drft_est |
| 20 |  | Upload CRS drift from FDF to ACU | a_crs_drft_upd |
| 21 |  |  |  |
| 22 |  | STEP 5: POST MANEUVER CONFIGURATION |  |
| 23 |  | Reset off-pointing flags. | a_pntg_flags |
| 24 |  | Start experiment off-pointing monitoring. | k_expop_mn_strt |
| 25 |  | Contact MDI and obtain approval to close the ISS loop. Then, proceed to close the ISS loop for MDI. | m_fl_issclos |
| 26 |  | Acquire additional tracking stars (use restricted search track when more than 3 stars are to be tracked). | a_ssu_st_set OR a_ssu_st_r |
| 27 |  | Declare stars eligible. | a_ssu_elig |
| 28 |  | Notify FDF of the final positions (slots) and magnitudes of all newly acquired stars, as necessary. |  |
| 29 |  | Enable reaction wheel speed limit update function. | k_rwslupd_ena |
| 30 |  | Start log_monitor to resume alert notifications. | o_start_logmon |
| 31 |  | STEP 6: INSTRUMENT RESTORAL |  |
| 32 |  |  |  |
| 33 |  | If ONLY a roll maneuver was performed, (no thruster actuations and SWAN was not safed), SKIP the following SWAN recovery activities: |  |
| 34 |  | Wait at least 2 hours AFTER last thruster firing before proceeding with any SWAN recovery actions. Return to NOMINAL limit set for SWAN, earliest 5 minutes prior to unlocking SWAN mechanisms. | o_esr_setlim (nom, swan) |
| 35 |  | Unlock SWAN mechanisms. WAIT AT LEAST 3 MINUTES before continuing with the start of nominal SWAN observations. | n_fl_llockout |
| 36 |  | Start SWAN observations. | n_fl_manrec |
| 37 |  |  |  |
| 38 |  | IF CDS was safed: Wait at least 2 hours AFTER last thruster firing, then open CDS doors. | c_fl_opendoors |
| 39 |  | IF CELIAS STOF was safed: Wait least 6 hours AFTER last thruster firing, then uplink recovery load, where nn is the version number. | o_dlydload (CELnn_RECOVR,n) |
| 40 |  | IF CELIAS MTOF was safed: Wait least 6 hours AFTER last thruster firing, then run procedure to recover MTOF. | f_fl_m_mnvrec |
| 41 |  |  |  |
| 42 |  | IF UVCS was safed via Patrol Safing Function: Contact UVCS team and enable NRT for recovery. | o_nrt_ena |
| 43 |  | IF UVCS was safed via u_fl_hvoff procedure: UVCS team will recover via NRT at a later date. |  |
| 44 |  |  |  |
| 45 |  | Wait at least 1 hour AFTER both CDS has opened doors AND UVCS recovery has been completed (if safed by Patrol Function), then run LASCO recovery procedure (or recover via NRT). | l_fl_recoverlasco |
| 46 |  | SCRIPT COMPLETE |  |