KARNATAKA POWER CORPORATION LIMITED

(A GOVERNMENT OF KARNATAKA ENTERPRISES)

MAHATHMA GANDHI HYDRO ELECTRIC POWER HOUSE

(CIN-U85110KA1970SGC001919)

Office of the Superintending Engineer (Elec.) MGHE Works, Jog Falls: - 577 435

No. L3MGS/HY/442			                                  		     	          Date: 06.11.2015

BRIEF “e” TENDER NOTIFICATION

(‘e’ TENDER NOTIFICATION NO: KPCL/2015-16/PS/WORK_INDENT3942 DT: 06.11.2015)

- Tenders in two covers are invited through “e” Procurement Portal                                       (Website URL:https://eproc.karnataka.gov.in) from the reputed Manufacturer/ contractor/agency/firm with proven track record of successful completion of similar works with adequate financial resources, past experience and suitable equipment’s for the following work in MGHE power house, Jogfalls-577 435,

| Sl. No | Name of the work | Approximate Cost put to tender in Rs. | EMD in Rs. | Tender processing fee in Rs. | Period of completion |
| --- | --- | --- | --- | --- | --- |
| 1 | Providing polymer based high performance corrosion protection epoxy coating on external surface of the penstock no. 1 from TB no 7 to 9, penstock no. 2 and 3 from TB no 6 to 9 and penstock no. 4 from TB no.6 to 8 in MGHE Power House, Karnataka Power Corporation Ltd, Jogfalls- 577435, Shimoga-Dist. ,Karnataka | 37,67,201/- | 75,350/- | 500/- | 2 Months |

- Tender documents can be downloaded from Government of Karnataka e-Procurement Website URL:https://eproc.karnataka.gov.in under login of bidders. After login, tender document can be downloaded from the portal within prescribed date and time published in the portal. Tenders must be electronically submitted (on-line through internet) with in the due date and time published in e-procurement portal

- Earnest Money Deposit (EMD) of Rs.75,350/-(Rupees Seventy Five Thousand Three Hundred Fifty Only) and tender processing fee should be paid online through e-Procurement portal using any of the payment modes like Credit Card, Direct Debit, National Electronic Fund Transfer (NEFT), Over the Counter (OTC). The transaction fee is non-refundable.

Contd..2

-2-

- THE BIDDERS SHALL HAVE THE FOLLOWING PRE-QUALIFYING REQUIREMENTS:

  - The Bidder shall be a regular Manufacturer/contractor/agency/firm and should have successfully carried out epoxy painting work on penstocks of power houses. In proof of the above, purchase order/work order/work completion certificate copies issued from competent authority should be furnished.

  - The Bidders in the last five financial years should have achieved in at least two financial years an average annual financial turnover of Rs.40.00 lakhs. In proof Annual Report/turn over certificates duly certified by chartered accountant shall be furnished.

  - Bidder shall have Independent PF registration certificate obtained from PF authorities, IT-PAN No, VAT No/ Service Tax Registration certificates. In proof PF registration, IT-PAN No, VAT No/ Service Tax Registration certificates copies shall be furnished.

  - The bid of the bidders whose contracts have been terminated/ foreclosed in Karnataka Power Corporation Ltd or elsewhere during last 05 years and also those who do not meet the above prequalifying requirement will be rejected.

  - Bidders have to compulsorily visit work site i.e., MGHE Power House, Karnataka Power Corporation Ltd., Jogfalls-577435, Karnataka before quoting to have hands on information about site conditions. The letter issued from Executive Engineer (Elect) MGHE  has to be enclosed as a proof of visiting the site.

- BRIEF SCOPE OF WORK:

The scope covers cleaning the external surface of the penstock pipes by sand blasting to achieve SA 2/2.5. The external surface should be free from abrasion, blisters, peeled off surfaces of the old paints, rusts etc., the full surface is to be cleaned until the parent metal is exposed for painting. Supply and conveyance of the paint with hardener, thinner and other materials etc as and when required to work spot. After cleaning, the surface should be applied with one coat of  epoxy primer paint of approved quality and two coats of high performance high solid anticorrosive approved epoxy coating followed by a coat of rust inhibitive compound, the thickness of the rust inhibitive compound coating should be 40 to 50 microns. The total thickness of the coating after two coats of epoxy painting and one coat epoxy primer paint  should be 250 microns. On application of polymer epoxy coating WFT (wet film thickness) is to be measured and recorded. On final curing DFT (Dry film thickness) is to be measured and recorded. All the materials required for surface preparation and coating shall be supplied by the Contractor.

- BID SCHEDULE:

| 1 | Last Date & Time for on-line submission of tenders | 04.12.2015 up to 16:00 Hrs |
| --- | --- | --- |
| 2 | Date & Time of opening the Technical Bid. | On. 07.12.20150at 16:30 Hrs |
| 3 | Date & Time of opening the Financial Bid. | On. 07.12.2015 at 16:45 Hrs if possible or any other convenient date which will be intimated separately. |

Contd..3

-3-

- PARTICULARS OF NOTIFICATION:

| ‘e’ Tender Notification No: KPCL/2015-16/PS/WORK_INDENT3642 Dtd: 06.11.2015 Name of work: Providing polymer based high performance corrosion protection epoxy coating on external surface of the penstock no. 1 from TB no 7 to TB no9, penstock no. 2 and 3 from TB no 6 to 9 and penstock no. 4 from TB no.6 to 8 in MGHE Power House, Karnataka Power Corporation Ltd, Jogfalls- 577435, Shimoga-Dist., Karnataka. | Tender Inviting Authority: The Superintending Engineer (Elec.) MGHE Works, Karnataka Power Corporation Limited Jog Falls.- 577435 Sagar – Tq, Shimoga – Dist, Karnataka Ph No :08186 - 244727 Fax No :08186 - 244753 Web Site: www.karnatakapower.com |
| --- | --- |

- After evaluation of Technical Bid and whose offer meet the PQR and technical specification of the tender/bid in complete manner will be accepted and only such bidders Financial bid will be opened.

- The quantity of materials and work mentioned/indicated in tender may vary depending on the actual requirement at the time of placing the work order.

- The bidder shall quote in Indian Rupees only. The bidder shall quote his rates including/inclusive of all the applicable taxes as per the latest GOK/GOI. orders.

- Right to accept or reject any or all the tenders without assigning any reason is reserved by the undersigned.

- KPCL reserves the right to verify the authenticity of any or all the certificates furnished by any or all the tenders from the authorities who have issued the same. If it is found that any of the agency/agencies have furnished false certificates/ information, the tenders submitted by them are liable for rejection.

- Further information if required can be obtained from office of the Superintending Engineer (Elec.), MGHE Works, KPCL, Jog falls – 577 435, Sagar – Tq, Shimoga – Dist, Karnataka or  HP HELPDESK 080-25501216/25501227

(R.Y Shirali)

Superintending Engineer (Elec.),

MGHE Works, Jog Falls - 577435.

Copy to      : 	Deputy Secretory (State Tender Bulletin Officer), Energy Dept. M. S Building, Bangalore – 01 – for kind information

:	District Commissioner (District Bulletin Officer), Shimoga Dist. – for kind information and wider publicity

:  MD/TD/FD – for kind information

:  ED(T)/ED(BTPS/ADPH) – for kind information.

:  CE(ED)/ECES/CE(O&M)/CEE/BTPS/ECEC-for kind information

:  SE(E)S/SE(E)GP/SE(E)V/SE(TA)/SE(E)Supa/SE(E)K/SE(E)N/SE(E)Almatti - for

Infomation.

:  AEE(SYSTEMS)JOG-along with soft copy of Bid Notification for publishing in KPCL Web site.

:  EE(MSP)J/EE(Technical Audit) Kargal - for information

: 	EE(E)MGHE/AGM(F)J for information with a request to present during opening of the tender.

:  AEE(SYSTEMS)JOG-along with soft copy of Bid Notification for publishing in KPCL Web site.

:  AO(IA) Kargal

:  Notice Board/ Docket/ MF/OC

KARNATAKA POWER CORPORATION LIMITED

(A GOVERNMENT OF KARNATAKA ENTERPRISES)

MAHATHMA GANDHI HYDRO ELECTRIC POWER HOUSE

(CIN-U85110KA1970SGC001919)

Office of the Superintending Engineer (Elec.) MGHE Works, Jog Falls: - 577 435

##### ABSTRACT “e” TENDER NOTIFICATION

(‘e’ TENDER NOTIFICATION NO: KPCL/2015-16/PS/WORK_INDENT3942	  DT: 06.11.2015)

Bids in two covers are invited through “e” Procurement Portal (Website URL:https://eproc.karnataka.gov.in) for the work of “ Providing polymer based high performance corrosion protection epoxy coating on external surface of the penstock no. 1 from TB no 7 to 9, penstock no. 2 and 3 from TB no 6 to 9 and penstock no. 4 from TB no.6 to 8 in MGHE Power House, Karnataka Power Corporation Ltd, Jogfalls- 577435, Shimoga-Dist., Karnataka.” from reputed bidders with proven track record of successful completion of similar works. Approximate cost put in to tender is Rs.37.67 Lakhs. Tenders must be electronically submitted (on-line through internet) with in the due date and time published in e-procurement portal. Earnest Money Deposit (EMD) of Rs75,350/- and tender processing fee should be paid online through e-Procurement portal. Last Date & Time for on-line submission of tenders is 04.12.2015 up to 16:00 Hrs. Date & Time of opening the Technical Bid is 07.12.20150at 16:30 Hrs. Further information if required can be obtained from office of the Superintending Engineer (Elec.), MGHE Works, KPCL, Jog falls – 577 435, Sagar – Tq, Shimoga – Dist, Karnataka Ph No: 08186-244727 or HP HELPDESK NO: 080-25501216/25501227.

(R.Y Shirali)

Superintending Engineer (Elec.),

MGHE Works, Jog Falls - 577435.

Cc to  :   ECES – for kind information

: 	AGM(CC)HO - B’lore – for information along with copy of Bid notification for      publishing in “Economics Times” News Paper, All India Metro Editions once.

:  Docket/MF/OC.