#### Cessna:  C182T (NAVIII)

CVD: 1 Dec 15   (G1000 & GFC700)

# Preflight Cabin

- AIF…Review all & Inspect for Airworthiness.

- Pitot Tube Cover…Remove & Check Clear.

- Documents	AROW in airplane

- POH & Garmin G1000™ Cockpit Ref. Guide ....... Accessible to Pilot.

- Parking Brake	Set.

- Control/Avionics Lock	Remove

- MAGNETOS Switch	Off.

- Avionics Switch (BUS 1&2)	Off.

- MASTER Switch (ALT & BAT)	On.

- Primary Flt Display	Verify On.

- FUEL QTY (L&R)	Check.

- LOW FUEL Annunciators	Off.

- OIL PRESS Annunciator	Verify On.

- LOW VAC Annunciator...Verify On.

- AVIONICS Switch (BUS 1)	On.

- Forward Avionics Fan…Check On (Listen).

- AVIONICS Switch (BUS 1)	Off.

- AVIONICS Switch (BUS 2)	On.

- Aft Avionics Fan…..Check On (Listen).

- AVIONICS Switch (BUS 2)	Off.

- PITOT HEAT Switch	On.

- PITOT HEAT/Stall Warning	Check.

- PITOT HEAT Switch	Off.

- Stall Warning System	 Check.

- LOW VOLTS Annunciator …Check On.

- Flap motor	Check at 10º-20º.

- Exterior lights	Check then off.

- MASTER Switch (ALT & BAT)	Off.

- Elevator & Rudder Trim	Takeoff position.

- FUEL SELECTOR Valve..	Both.

- ALT STATIC AIR Valve…..Off (Push In).

- Fire Extinguisher	Check (Verify green).

Preflight Empennage

- Baggage Door…………Check (Secure).

- Rudder Gust Lock……….Remove.

- Tail Tie-Down	Disconnect.

- Tail Streamer…………… Remove.

- Control Surfaces	.Check.

- Trim Tab	Check for security.

- Antennas	Check.

Preflight Right Wing trailing edge

- Flap	Check Condition.

- Aileron	Check Movement.

- Wingtip/Lights 	Check Condition.

# Preflight Right Wing

- Wing Tie Down	Disconnect.

- Fuel Tank Vent Opening	Check.

- Main Wheel Tire (42 PSI)….Check.

- Brake………………Check Visually.

- Chocks…………..Remove & Stow.

- Fuel Tank Sump Quick Drain Valves (5)	Drain.

- Fuel Quantity ……..Check Visually

- Fuel Filler Cap…Secure and Vent Clear

Nose

- Static Source Opening (Right)	Check.

- Fuel Strainer Quick Drain Valves (3).	Drain.

- Engine Cooling Air Inlets…..Check.

- Propeller & Spinner	Check.

- Air Filter	Check.

- Nosewheel Strut/Tire(49PSI)Check.

- Tow Bar/Chocks…Remove & Stow.

- Engine Cooling Outlets	Clear.

- Engine Oil Dipstick	Check oil level & secure (4 qt min., 9 qt for extended flights).

- Static Source (Left)………….	Check.

# Preflight Left Wing Leading Edge

- Fuel Tank Vent Opening	Check.

- Stall Warning Vane...	Check.

- Land/Taxi light(s)…Check condition.

- Wingtip/Lights..…..Check Condition.

# Preflight Left Wing

- Wing Tie-down	Disconnect.

- Left Fuel Quantity	Visually Check.

- Fuel Filler Cap	Secure.

- Fuel Tank Sump Quick Drain Valves (5)	Drain.

- Main Wheel Tire (42 PSI)	Check.

- Brake………………..Check Visually.

- Chocks…………….Remove & Stow.

# Preflight Left Wing Trailing Edge

- Left Aileron	.Check Movement.

- Left Flap	.Check Condition.

- Baggage Door…Re-check (Secure).

Before Starting Engine

- Preflight Inspection	Complete.

##### PASSENGER BRIEF

- Seat Belts / Shoulder Harness

- Personal Electronic Devices off

- Air Vents / Comfort

- Fire Extinguisher Location / Operation

- Emergency Procedures & Exits

##### MISSION BRIEF

- Mission Objective

- Destination, WX, Route, Alt, ETE

- NOTAMS

- Crew Coordination & CRM

- Sterile Cockpit Procedures

- Cockpit Layout

- Intercom & Radio Usage

- Seats, Seatbelts, Doors

- Emergency Action & Equipment

- Passenger Brief	Complete.

- Sterile Cockpit……………...Comply.

- Seats / Belts / Shoulder Harness	Adjust and lock, check inertial reels.

- Brakes	Test & Set.

- Circuit Breakers	Check In.

- Electrical Equipment	Off.

Caution (See Complete Caution in POH)

The avionics switch (Bus 1 and 2) must be off during engine start to prevent possible damage to avionics.

- Avionics Switch (Bus 1&2)…….Off.

- Cowl Flaps……………………Open.

10. Fuel Selector Valve…………. Both.

# Starting Engine (Using Battery)

- Throttle Control	Open ¼ Inch.

- Propeller Control	High RPM.

- Mixture Control	Idle Cut Off.

- Stby Batt Switch	Test and Arm

Hold for 10 seconds, verify that green test lamp does not go out, then ARM and verify that PFD comes on).

- Engine Indicating System	Check.

parameters, (verify no red X’s through 		ENGINE page indicators).

- Bus E Volts	24 volts min.

- M Bus Volts…Verify 1.5 volts or less.

- Batt S Amps	Discharge (neg).

- Stby Batt Annunciator	On.

- Propeller Area	Clear.

- Master Switch (Alt and Bat)	On.

- Beacon Light Switch…	On as required.

Note

If engine is warm, omit priming procedure of steps 13, 14 and 15 below.

- Fuel Pump Switch	On.

- Mixture Control..	.Advance to Full Rich, wait until fuel flow indication is stable, and then return to idle cut off position.

- Fuel Pump Switch	Off.

- Magnetos Switch	Start.

- Mixture Control..	..Advance to full rich when engine starts.

Note

If the engine floods, place the mixture control in the Idle Cut Off position, open the throttle control ½ to full, and engage the starter motor (Start).  When the engine starts, advance the mixture control to the Full Rich position and retard the throttle control promptly.

- Oil Pressure	Check.

- Amps (M Batt & Batt S)	Check.

charge (positive).

- Low Volts Annunciator	Verify Off.

- Nav Lights Switches	On as req.

- Avionics Switch (Bus1&2)	On.

- Mission Master Switch…………On.

- Transponder... TEST/Code Set/ALT.

- Check MFD for correct A/C type and Navigation database expiration dates, then press ENT.

- Fuel Totalizer…………….…Reset.

- ATIS / AWOS	Copy.

- G1000 Flight Plan…Enter as Req’d.

- Altimeters: PFD & Standby…..Set.

Taxi

- Brakes	Test.

- Heat / Vents / Defrost	As Required.

- Attitude Indicator. 	Verify Proper Ops.

- Turn Coordinator. Verify Proper Ops.

- HSI &Compass….Verify Proper Ops.

Before Takeoff - Run-Up

- Parking Brake	Set.

- Passenger Seat Backs	Upright pos.

- Seats and Seat Belts	Secure.

- Cabin Doors	Closed and Locked.

- Flight Controls	Free & Correct.

- Flight Instruments	Check no red Xs.

- Altimeters Recheck:

- PFD (Baro)	Set.

- Standby Altimeter	Set.

- Altitude Select	Set.

- Standby Flight Instruments	Check.

- Fuel Quantity	Check.

Note 1

Flight is not recommended when both fuel quantity indicators are in the yellow arc range.

- Autopilot	ENGAGE verify can …………overpower in pitch and roll

- Autopilot Trim DISC Button verify aural alert and………Off.

- Flight Director	.Off.

- Electric/Manual Trim………..Check.

- Elevator & Rudder Trim for Takeoff.

- Mixture	.Rich.

- Throttle Control	1800 RPM.

- Magnetos Switch	Check (RPM drop 175 or 50 differential between magnetos.)

- Prop Control	..Cycle from high to low RPM, return to high RPM.

- VAC Indicator	Check.

- Engine Indicators……...Check.

- Ammeters & Voltmeters.	Check.

- Annunciators...Check (none shown).

- Throttle	Check Idle.

- Throttle	1000 RPM or less.

- Throttle Friction Lock	Adjust.

- Mixture…Ground Lean as Required.

- Com Frequency(s)	Set.

- Nav Frequency(s)	Set.

- FMS/GPS Flight Plan	As Desired. NOTE: Check GPS 1 & 2 status

- XPDR (Transponder)...Code Set/ALT.

- CDI Softkey	Select NAV source.

Caution: (See Full Caution in POH)

The G1000 HSI does not provide a warning “Flag”. The missing D-Bar is considered to be the warning flag.

- Cabin Power 12V Switch……...Off.

- Wing Flaps.. UP 0°-20° (10º preferred).

- Cowl Flaps	Open.

- Cabin Windows	Closed & Locked.

- Strobe/Pulse Lights Switch	On.

- Brakes	Release.

Takeoff

- Flaps	0°-20° (10º preferred).

- Short Field T.O.	20° Flaps / 58

KIAS Until Clear.

- Soft Field T.O.	20° Flaps/Ground

Effect ASAP.

- Throttle Control	Full.

- Propeller Control	2400 RPM.

- Mixture Control	….Full Rich

(above 5000 ft. alt., lean for max. RPM.)

- Rotate	50-60 KIAS.

- Normal Climb Speed	80 KIAS.

- Flaps…….. Retract above 70 KIAS. At safe altitude

After Takeoff and Climb

- Airspeed	85-95 KIAS.

- Throttle	..23 Inches or Full.

(If less than 23 in. Hg.).

- Propeller Control	2400 RPM.

- Mixture……….15 GPH or Full Rich

(If less than 15 GPH).

- Fuel Selector Valve …Both

- Cowl Flaps	Open or as required.

- Mission Master Switch....………On.

- Sterile Cockpit…………..Terminate.

Cruise

- Power...15-23 In. at 2000-2400 RPM (no more than 80%).

- Elevator & Rudder Trim	Adjust.

- Mixture	Lean.

- Cowl Flaps	As required.

- FMS/GPS..	Review & Brief.

- Auto Pilot…………..…..As desired.

Descent

- Power	As Desired.

- Mixture	 Adjust as necessary.

- Cowl Flaps	Closed.

- Altimeters:

- PFD (Baro)	Set.

- Standby Altimeter	Set.

- G1000 Alt Select	Set.

- CDI Softkey	Select NAV source.

- FMS/GPS 	Review & Brief.

See Caution in Before Takeoff Run-up.

- Fuel Selector Valve	Both.

## Wing Flaps	As desired.

## Before Landing

- Sterile Cockpit……………Comply.

- Pilot & Passenger Seat Backs……..Upright Position.

- Seats & Seat Belts	Secured & Locked.

- Fuel Selector………………... Both.

- Mixture Control	Rich.

- Propeller Control	High RPM.

- Landing & Taxi Light Switches	On.

- Autopilot	Off.

- Cabin 12V Power Switch…..…Off.

Normal Landing

- Airspeed	70-80 KIAS (Flaps Up).

- Wing Flaps	As Desired.

- Airspeed	60-70 KIAS (Full Flaps).

- Trim	Adjust.

- Touchdown	Main Wheels First.

- Landing Roll	…Gently Lower Nose.

- Braking	…..Min Required.

## Balked Landing

- Power…Full Throttle  Control & 2400 RPM.

- Go Around Button…………Press.

- Wing Flaps…… Retract to 20°

- Climb Speed	55 KIAS.

- Wing Flaps-Retract Slowly (above 70 KIAS).

- Cowl Flaps	Open.

After Landing (Clear of Runway)

- Wing Flaps	Up.

- Cowl Flaps	Open.

- Lights	As Required.

- Pitot Heat	Off.

- Mixture…Lean as desired for GND Ops.

# Securing Aircraft

- Parking Brake	Set.

- ELT 406 MHz ……………..Check.

- Throttle Control (1800 for 15 secs) then 	Idle (if clear behind & practicable).

- Electrical Equipment	Off.

- Avionics Switch (Bus 1&2)	Off.

- Magnetos	Check for Ground.

- Mixture	Idle Cut-Off.

- Sterile Cockpit…….…Terminate

- Magnetos (Ignition) Switch	Off.

- Master Switch (ALT/BAT)	Off.

- Hobbs, Tach and Fuel…..Record.

- Stby Batt Switch	Off.

- Control/Avionics Lock	Install.

- Cowl Flaps 	Closed.

- Fuel Selector	Left or Right.

- Chocks……………………...Install.

- Parking Brake 	 Off.

- Aircraft	Secured & Locked.

- Flight Plan & FRO	Closed.

General...

- EMERGENCY	121.50

- Unicom	122.70-122.80-122.95

123.00-123.05

- Multicom	122.90

- Flight Service	122.20 (Most Common) 122.10-122.60-123.60

- Air to Air	122.75-122.85-123.45

Transponder Codes

- VFR Transponder……………....1200

- Lost Comm.……………….…....7600

- Emergency………………………7700

- Hijack…………………………….7500

This checklist is a guide to coordinate Pilot Operating Handbook and STC data applicable to this particular aircraft only.  The applicable Pilot Operating Handbook and STC installations remain the official documentation for this aircraft.  The pilot in command is responsible for complying with all items in the Pilot Operating Handbook and applicable STCs.

# Text boxes

WARNING

When the master switch is on, using an external power source, or manually rotating the propeller, treat the propeller as if the magnetos switch were on. Do not stand, nor allow anyone else to stand, within the arc of the propeller since a loose or broken wire, or a component malfunction could cause the engine to start.

See Fuel Contamination Warning in the POH.

See Fuel Contamination Warning in the POH.

See Fuel Contamination Warning in the POH.

WARNING

(See Full Warning in POH)

Interruption of NAV signal to the autopilot will cause autopilot to revert to ROL mode with NO warning chime or PFD annunciation.

See Warning in Before Takeoff-Run-up.