DATE	10th march 2009

FROM	ITALPRESSE S.P.A.

# TO	SCOTT AND SARGEANT

ATT.	Mr. MARK GIBSON

RE.	Press line mod. MARK/C 16-26/7

Dear Mr. Mark,

Following your request , please find here our offer for an automatic press line mod. MARK/C 14-26/7.

In alternative we can offer a through feed press type

MARK-C 20-30/7 with platen dimensions  2000 x 3000 mm.  at

PRICE € 162.100,00

We are at your full disposal for any further information your might need.

Best regards

###### Antonio Locatelli

AUTOMATIC FLOW LINE MOD. MARK/C 16-26/7

composed of:

POS.  1 LOADING BELT MOD. NC 16-31

- dimensions                              mm.   1600X3100

- translation speed                       mt/1'      0-40

- panels translation synchronized with

press belt

- manual control with pedal for

advancement and reversal

- electric eyes                           nr.           2

POS. 2 AUTOMATIC PRESS MOD. MARK/C 16-26/7

- platens dimensions                      mm.   1600X2600

- daylight opening                        mm.         140

- loading on side of                      mm.        1400

- down stroking movement of the platens

- solid drilled platens - thickness       mm.      90/110

- type of heating: NOT INCLUDED

customer will heat the press

with the steam

- total pressure                          Tons        233

- specific pressure on 80% of the

surface                                 Kg/cm2        7

- pressure pistons dia. mm. 125           nr.           8

- mouvement pistons                       nr.           2

- pistons stroke                          mm.         140

- closing time                            sec.          2

- opening time                            sec.          3

- time to reach the pressure              sec.          3

- speed of the belt inside the press      mt/1'      0-40

- belt control with self braking

motor reducer group

- racks group with torsion rods

ITALPRESSE PRESS CHARACTERISTIC

RING FRAME, PLATENS, CYLINDERS and ASSEMBLED GROUP

The press structure is made of CNC machined components to assure an accurate assembling.

1. Ring frame

The solid profiled steel frames are made by S275JR steel sheet which is oxygen cut and subsequently CNC machined according the project drawings and data

2. Platens

Made by S 275 JR

Solid platens worked by deep-hole drilling machine to guarantee:

- the constant control of the bore axis in order to obtain a uniform platen temperature

- optimised bore diameter in relation to the head loss((p) and in relation to the required loss of temperature ((t)

- the heating circuit is obtained with the intersection of the two perpendicular bore directions and by inserting steel blocks in order to drive the heating oil.

The number of the inlet and outlet for the heating fluid is optimised in relation with the press application.

This guarantee a temperature over every area of the platens according to the specific needs.

3. Cylinders

The  cylinder liner is made of S 355 JR  steel.

The stem is made of 40NiCrMo4 alloy steel

All the cylinders are produced by a robot welding centre and the face is realised in controlled atmosphere with a constant control of:

- speed rotation

- atmosphere pressure and quality

- torch temperature

The cylinders are examined with non-destructive tests using X-ray or magnetic resonance.

The cylinders pass the quality control test only if the parameters are the following:

- surface hardness of the stem Cr face: 	74-78 HRC

- stem surface finish:					Ra = 0.8 micron

- roundness tolerance:				     mm 0.04

All welded components are normalised in order to avoid internal stresses.

4. Assembled group

The RING FRAME-CYLINDERS-PLATENS group is assembled to compensate and reduce problems such as:

- thermal expansion

- synchronous and parallel movement of the platen

- stem overheating

Concerning the stem overheating effect, in our presses mod. MARK, we avoid stem-platen direct contact by inserting:

- insulating material with high specific pressure resistance

- solid drilled plates to avoid the hydraulic oil heating due to the stem heating

The stem is "mechanically anchored" to allow sliding in any direction in order to compensate thermal expansions.

All the components, which allow the platen movement, are linked so

that the platen moves perfectly parallel.

The RING FRAME-CYLINDERS-PLATENS group is assembled without welding to allow thermal expansion in any directions.

The press will be completed with the following main devices:

POS.2.1 DOWNSTROKING BRAKE to decelerate the closing speed of the

mobile platen for a soft contact with the panels

POS.2.2 FLATNESS CONTROL, which,  besides  the  mechanical  group

with racks and pinion, guarantees a constant  control  of

the mobile   platen  flatness to avoid any trouble if for

any reason the platen does not go down parallel.

POS.2.3 ELECTRO-PNEUMATIC DEVICE for   top  mylar   belt shaking,

running at every press opening   (at   the   end   of the

pressing cycle) to guarantee the detaching of the pressed

panel

POS.2.4 COOLED PLATES for the insulation of the pressure

cylinders:

with first layer of insulating material and second of

solid steel drilled for water circulation.

The plates are connected with inlet and outlet main

pipes.

POS. 2.5 MANIFOLDS

POS.  3 UNLOADING GRAVITY ROLLERS MOD. NC 16-31

- dimensions                              mm.   1600X3100

POS.  4 CONTROL BOARD

- complete with all the electric and programmable

logic electronic equipments to test and control

the whole line

TOTAL PRICE                                        EURO 119,500,00

SUPPLY CONDITIONS

DISCOUNT			25%

DELIVERY			EX WORKS our factory

##### DELIVERY TIME	About 150 days from receipt of order and down payment (August excluded)

PAYMENT			30% Down Payment at the order

70% Bank transfer before shipment

SET UP	ITALPRESSE will send one technician at the cost of EURO 8,900 net (board and lodging at your charge)

OFFER VALIDITY		60 days

# Text boxes

ITALPRESSE S.p.A.

Via delle Groane, 15 - Bagnatica (BG) - 24060 - ITALIA

TEL.  :  (+39) - 035 - 68 11 22      FAX.  :  (+39) - 035 - 682  682

e-mail	:  sales@italpresse.com

ITALPRESSE

Woodworking

machinery