OPC Namespace Definition

for Road Construction Machinery

Draft Version

Version 0.1

Date: 29. January 2003

Contents

1	Scope	3

2	References	3

3	Abbreviations	3

4	Operating principles	4

5	Error handling	5

6	Namespace definition	6

1	Scope

This OPC namespace definition specifies the communication behaviour of OSYRIS compliant modules.

This document was developed by the OSYRIS (Open System for Road Information Support) consortium (www.osyris.org).

2	References

[1]	OPC Data Access Custom Interface Standard, Version 2.04, OPC Foundation 2000

[2]	OPC Data Access Automation Interface Standard, Version 2.02, OPC Foundation 1999

3	Abbreviations

CES

Compaction Expert System

GUI

Graphical User Interface

MMI

Men-Machine-Interface

OLE

Object Linking and Embedding

OPC

OLE for Process Control

OSYRIS

Open System for Road Information Support

4	Operating principles

The OPC server behaviour described in this document is used on mobile road construction machinery as a base of data exchange of the onboard computer. Several clients can be modularly connected to it, providing and requesting data. Such components can be

- one or more fieldbus sources

- one or more positioning components

- calculation components like filters and simulators

- communication components for data transfer to other machines

- GUI components

The OPC server supports both the OPC Data Access Custom Interface Standardand the OPC Data Access Automation Interface Standard.

Additionally to the standard OPC quality system, an improved and more detailed error handling is created for OPC servers on road construction machinery due to the high requirements in such an environment. The quality flags are used as shown below:

To increase the functionality and robustness of the system, the system supports the exchange of hardware (e.g. sensors) during the work progress. Therefore the OPC server creates all possible items and groups even if the corresponding data sources are not connected. If a data source is found, the quality flag of this item changes as described in chapter 5.

Alternative data sources and 'unqualified items'

Due to the possibilities of the usage of different data sources for each piece of data, the OPC server must provide the handling of priority lists for each item. When the quality of an item changes to bad, the server has to suggest another 'alternative' item to connected clients using the event group as described in chapter 5.

The OPC server offers a mechanism for clients to connect to items using a simple name. When a client connects to a item and needs the item with the best quality, the item specified by the client can be an 'unqualified item' which is the item's name without a group name.

Example:

the unqualified item named 'Speed' gets either connected to

'Manual.Speed',

'Fieldbus.Speed',

'Position.Speed' or

'Default.Speed',

depending on the availability.

Timeout

For each created item a timeout value can be created. The server changes the quality flag from 'good' to 'last usable' (44h) after the timeout has occurred. All timeout values are specified in milliseconds.

5	Error handling

Additionally to the standard quality flags of each OPC item, the following items are created to signal connected components more specific information about occurring errors:

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Event | Number | Int4 | Number of the event, increased by the occurrence of each event |
|  | Type | Int4 | Specifies the type of the event: 0: unspecified, 1: quality changes from good to bad, 2: quality changes from bad to good, 3: written by clients to set the quality of an item |
|  | OldName | String | name of the item which quality changes |
|  | NewName | String | proposition of an item to use instead |
|  | OldShortName | String | unqualified item name (see operation principles) |
|  | Quality | Int4 | quality value to be set (use with event type 3) |

Priority lists for different OPC items

unqualified item name: Speed

- Manual.Speed

- Position.Speed

- Fieldbus.Speed

- Default.Speed

unqualified item name: Temperature

- Manual.Temperature

- Fieldbus.Temperature

- Designed.Temperature

- Default.Temperature

unqualified item name: Thickness

- Manual.Thickness

- Fieldbus.Thickness

- Designed.Thickness

- Default.Thickness

6	Namespace definition

6.1	Overview

The OPC server creates the following groups, which are described in detail in this chapter:

- 'Default'

- 'Designed'

- 'Manual'

- Event'

- 'Fieldbus'

- 'FieldbusOut'

- 'Position'

- 'Positioning3D'

- 'Compaction'

6.2	Group 'Default'

This group contains default values of several items which are set by the server. The quality of the items must always be good.

Number of items: 3

Timeout: 0

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Default | Speed | Real8 | default speed value, [m/s] set to 50 on start-up |
|  | Temperature | Real8 | default ambient temperature value, [°C] set to 20 on start-up |
|  | Thickness | Real8 | default thickness value, [mm] set to 40 on start-up |

Remarks:

The quality of these items is set to 'good' (C0h) on start-up and is not to be changed.

6.3	Group 'Designed'

This group contains items which specify the value of the road design for the current position. These values are written by a client which is connected to the design database.

Number of items: 6

Timeout: 0

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Designed | Roll | Real8 | angle position, rotating around longitudinal axis, [rad, clockwise = negative] tTimeout 20 s |
|  | zLeft | Real8 | surface height on the left side, [0.1 mm] timeout 20 s |
|  | zRight | Real8 | surface height the right side, [0.1 mm] timeout 20 s |
|  | Temperature | Real8 | material temperature value, [°C] |
|  | Thickness | Real8 | thickness of the layer [0.1 mm] |
|  | LongSlope | Real8 | longslope [0.01 %, up = positive] |

6.4	Group 'Manual'

The items in this group are written by the user of the machine through the GUI client. The quality of the values can be set manually by the user using events.

Number of items: 7

Timeout: 0

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Designed | Speed | Real8 | speed [m/s] |
|  | Temperature | Real8 | material temperature [°C] |
|  | Thickness | Real8 | layer thickness [0.1 mm] |
|  | StartAbscissa | Real8 | abscissa (longitudinal position) [mm] |
|  | StartOffset | Real8 | offset (lateral position)[mm] |
|  | AmbTemperature | Real8 | ambient temperature [°C] |
|  | AmbWind | Real8 | ambient wind speed [m/s] |

6.5	Group 'Event'

see chapter 5 for description

6.6	Group 'Fieldbus'

The entries of this group are written either by the server if it is connected to the fieldbus itself or by a client which has a connection.

Number of items: 58

Timeout: 2000 ms

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Fieldbus | MachType | Int2 | machine type |
|  | E | Real8 | 3D absolute position, east direction [m] |
|  | N | Real8 | 3D absolute position, north direction [m] |
|  | H | Real8 | 3D absolute position, height [m] |
|  | Pitch | Real8 | angle position, rotating around lateral axis, [rad, up = positive] |
|  | Roll | Real8 | angle position, rotating around longitudinal axis, [rad, clockwise = negative] |
|  | Yaw | Real8 | angle position, rotating around vertical axis, [rad, north = 0, west = pi/2] |
| Fieldbus | Distance | Real8 | travelled distance including DistanceH [m] |
|  | DistanceH | Real8 | travelled distance, increases every 232 mm by one |
|  | Abscissa | Real8 | longitudinal position on the track [m] |
|  | Ordinate | Real8 | lateral position on the track [m] |
|  | LevelDevL | Real8 | deviation of the surface level on the left side [mm] |
|  | LevelDevR | Real8 | deviation of the surface level on the right side [mm] |
|  | Speed | Real8 | speed [m/s] |

| Fieldbus | DrumRotationsRes | Real8 | compactor specific: resolution of the drum rotation encoder [pulses per rotation] |
| --- | --- | --- | --- |
|  | DrumRotationsF | Real8 | compactor specific: drum rotation front wheel [pulses] |
|  | DrumRotationsB | Real8 | compactor specific: drum rotation rear wheel [pulses per rotation] |
|  | DrumRotation SpeedRes | Real8 | compactor specific: resolution of the drum rotation encoder [pulses per rotation] |
|  | DrumRotation SpeedFront | Real8 | speed front wheel [pulses/s] |
|  | DrumRotation SpeedBack | Real8 | speed rear wheel [pulses/s] |

| Fieldbus | TowSlopeL | Real8 | slope of the left tow-arm [1] |
| --- | --- | --- | --- |
|  | TowSlopeR | Real8 | slope of the right tow-arm [1] |
|  | Thickness | Real8 | average thickness [mm] |
|  | ThicknessR | Real8 | thickness on the right side [mm] |
|  | ThicknessL | Real8 | thickness on the left side [mm] |
|  | Evenness | Real8 | evenness [1] |
|  | WidthL | Real8 | left screed width incl. extension [m] |
|  | WidthR | Real8 | right screed width incl. extension [m] |
|  | Width | Real8 | total screed width [m] |
|  | VolumeTotal | Real8 | total volume [m³] |
|  | Volume | Real8 | volume of the current mission [m³] |

| Fieldbus | Temperature | Real8 | average material temperature [°C] |
| --- | --- | --- | --- |
|  | TemperatureL | Real8 | material temperature on the left side [°C] |
|  | TemperatureR | Real8 | material temperature on the right side [°C] |
|  | TemperatureM | Real8 | material temperature in the mid [°C] |
|  | AmbTemperature | Real8 | average ambient temperature [°C] |
|  | AmbTemperature1 | Real8 | ambient temperature measurement [°C] |
|  | AmbTemperature2 | Real8 | ambient temperature measurement [°C] |
|  | TempBase | Real8 | temperature of the base layer in front of the paver [°C] |
|  | TempSurface | Real8 | temperature of the surface below machine (the new layed layer) [°C] |
|  | AmbWind | Real8 | average speed of the ambient wind [m/s] |

| Fieldbus | PreCompaction | Real8 | precompaction value [1] |
| --- | --- | --- | --- |
|  | Compaction | Real8 | compaction value [1] |
|  | Passes | Real8 | number of roller passes at current pos. [1] |
|  | RollingResistance | Real8 | rolling resistance value [N] |
|  | PressureF | Real8 | oil pressure in front hydraulic drive system [kPa] |
|  | PressureB | Real8 | oil pressure in back hydraulic drive system [kPa] |
|  | VertDistanceF | Real8 | distance from the chassis to the surface at the front of the machine [m] |
|  | VertDistanceB | Real8 | distance from the chassis to the surface at the back of the machine [m] |

| Fieldbus | VertAccelFL | Real8 | vertical acceleration during the vibratory compaction (front left) [m/s²] |
| --- | --- | --- | --- |
|  | VertAccelFR | Real8 | vertical acceleration during the vibratory compaction (front right) [m/s²] |
|  | VertAccelBL | Real8 | vertical acceleration during the vibratory compaction (back left) [m/s²] |
|  | VertAccelBR | Real8 | vertical acceleration during the vibratory compaction (back right) [m/s²] |
|  | VibrationFreq | Real8 | vibration frequency [1/s] |
|  | TamperFreq | Real8 | tamper frequency [1/s] |

6.7	Group 'FieldbusOut'

All values written to this group are transmitted to the fieldbus either by the server itself or any connected fieldbus client.

Number of items: 11

Timeout: 3000 ms

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| FieldbusOut | Event | Int4 | Event description, see "CANopen Device Profile for Road Construction Machinery" |
|  | E | Real8 | 3D absolute position, east direction [m] |
|  | N | Real8 | 3D absolute position, north direction [m] |
|  | H | Real8 | 3D absolute position, height [m] |
|  | Distance | Real8 | travelled distance [m] including DistanceH |
|  | DistanceH | Real8 | travelled distance, increases every 232 mm by one |
|  | Abscissa | Real8 | longitudinal position on the track [m] |
|  | Ordinate | Real8 | lateral position on the track [m] |
|  | LevelDevL | Real8 | deviation of the surface level on the left side [mm] |
|  | LevelDevR | Real8 | deviation of the surface level on the right side [mm] |
|  | Speed | Real8 | speed [m/s] |

6.8	Group 'Position'

This group contains the current 'true' position of the machine. The data is written by a positioning client that uses information from the fieldbus, a GPS or a total station to calculate and filter the position data.

Number of items: 13

Timeout: 3000 ms

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Position | E | Real8 | 3D absolute position, east direction [m] |
|  | N | Real8 | 3D absolute position, north direction [m] |
|  | H | Real8 | 3D absolute position, height [m] |
|  | Pitch | Real8 | angle position, rotating around lateral axis, [rad up = positive] |
|  | Roll | Real8 | angle position, rotating around longitudinal axis, [rad, clockwise = negative] |
|  | Yaw | Real8 | angle position, rotating around vertical axis, [rad, north = 0, west = pi/2] |
|  | Distance | Real8 | travelled distance [m] |
|  | Speed | Real8 | speed [m/s] |
|  | Abscissa | Real8 | longitudinal position on the track [m] |
|  | Ordinate | Real8 | lateral position on the track [m] |
|  | NumPos | Int4 | number of the position, increased with each position [1] |
|  | Flags | Int4 | see below |
|  | FlagsStr | String | see below |

Flags for Positioning:

The following masks define private flag bits to be used in appropriate subsystems. Elsewhere they are ignored.

| Position.Flags | Position.FlagsStr | Description |
| --- | --- | --- |
| 0000 0000h | POS_INVALID | invalid position |
| 8000 0000h | POS_VALID | valid position |
| 0000 0001h | POS_STOP | machine stopped |
| 0000 0002h | POS_FORWARD | machine moves forward |
| 0000 0004h | POS_BACKWARD | machine moves backward |
| 0000 0080h | POS_VIBRATING | roller in vibrating mode |
| 0000 0020h | POS_ERROR_HEADING | no clear heading of the machine available |
| 0000 0100h | POS_ACCURACY_LOW | low accuracy of the calculated position |
| 0000 0200h | POS_ACCURACY_MED | medium accuracy of the calculated position |
| 0000 0400h | POS_ACCURACY_HIGH | high accuracy of the calculated position |
| 0000 0800h | POS_GPS_SHADOW | position in GPS shadow zone |

6.9	Group 'Positioning3D'

The items in this group are written by a client connected to a (robotic) total station (TCA).

Number of items: 4

Timeout: 3000 ms

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Positioning3D | HorizAngle | Real8 | Horizontal angle to the reflector from the TCA [°] |
|  | VertAngle | Real8 | Vertical angle to the reflector from the TCA [°] |
|  | Distance | Real8 | Distance to the reflector [m] |
|  | Precision | Int4 | Precision of the TCA |

6.10	Group 'Compaction'

This group contains information about the compaction done by the machine or information to obtain such data.

Number of items: 17

Timeout: 100.000 ms

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Compaction | RollResistanceLoc | Real8 | Rolling Resistance |
|  | RollResistance | Real8 | Rolling Resistance |
|  | Compaction | Real8 | compaction value [1] |
|  | Passes | Real8 | number of passes at the current position [1] |
|  | Grade | Real8 | compaction grade |

| Group | Item | Type | Description |
| --- | --- | --- | --- |
| Compaction | AL | Real8 | see below |
|  | BL | Real8 | see below |
|  | AM | Real8 | see below |
|  | BM | Real8 | see below |
|  | AR | Real8 | see below |
|  | BR | Real8 | see below |
|  | TimeToCompactL | Real8 | Time left to compact on the left side of the screed (paver only) [s] |
|  | TimeToCompactM | Real8 | Time left to compact in the mid of the screed (paver only) [s] |
|  | TimeToCompactR | Real8 | Time left to compact on the right side of the screed (paver only) [s] |
|  | Temperature | Real8 | Temperature [°C] |
|  | TimeLeft | Int4 | Time left to compact [s] |
|  | RRNumPos | Int4 | NumPos for RR |

The items AL to BR give the description of the cooling curve of the asphalt and are the coefficients in the equation  Temperature = b ·ea·Time . The indication L, M and R describes the position of the cooling curve.