** INSTALLATION INSTRUCTION MANUAL**

** topics **                                                           page#

- PRISM MONITOR INSTALLATION  --------------------------------------------2

- WIRING INSTRUCTIONS ----------------------------------------------------------3

- SERIES 6000 PRISM CABLING DIAGRAMS---------------------------------- 4

- SERIES 500 PRISM CABLING DIAGRAMS-------------------------------------5

- CONNECTOR SPECIFICATIONS------------------------------------------------- 11

- SENSOR SPECIFICATIONS --------------------------------------------------------6

- PRISM DISPLAY OPERATIONS ------------------------------------------------- 13

- AIR RELIEF VALVE MOUNTING------------------------------------------------14

NOTE:  The Prism CANNOT be calibrated in the field.  Attempting any calibration can cause permanent damage to the Prism and void its warranty.  If you believe the Prism has a problem, contact M.C. Products at 1-800-345-0839 and speak with a technician.  Thank you.

*PRISM INSTALLATION INSTRUCTIONS**

**PRISM WIRING INSTRUCTIONS**

** MONITOR SPECIFICATIONS**

| /////////////////////////////// | 500 PRISM | 2000 PRISM |
| --- | --- | --- |
| CURRENT LOAD | 1.25A | 1.25A |
| SUPPLY VOLTAGE | 12V/24V | 12V/24V |
| SYSTEM GROUND | NEG/POS | NEG/POS |
| SENTINEL LOAD | .05A | .05A |

**CONTROL CABLE SPECIFICATIONS**

| PURPOSE | TYPE | LENGTH | CONNECTORS | PART# |
| --- | --- | --- | --- | --- |
| EXTENSION | REMOTE TO MASTER | 11 ft. | MALE/FEMALE DEUTSCH 5-CONDUCTOR | M1404 |
| EXTENTION | EXTENSION | 15 ft. | MALE/FEMALE DEUTSCH 4- CONDUCTOR | M1145 |
| EXTENTION | “Y” CONNECTOR | 6( | MALE/MALE/FEMALE DEUTSCH (SENSOR TO MASTER & REMOTE) | M1412 |

**SERIES 2000 PVC SENSOR SPECIFICATIONS**

| SENSOR TYPE | CABLE LENGTH | MALE CONNECTOR | FLANGE DIAMETER | LENGTH |
| --- | --- | --- | --- | --- |
| TOP MOUNT 4 BOLT | 1 ft. | GRAY DEUTSCH 4 PIN CONNECTOR (MALE) DT04-4P | 2.5( | CUSTOM SIZED |
| SIDE MOUNT 4 BOLT | 1 ft. | GRAY DEUTSCH 4 PIN CONNECTOR (MALE) DT04-4P | 2.5( | 6( |

**STAINLESS STEEL SENSOR SPECIFICATIONS**

(SERIES 500 WATER ONLY)

| SENSOR TYPE | CABLE LENGTH | MALE CONNECTOR | FLANGE DIAMETER |
| --- | --- | --- | --- |
| TOP MOUNT 4 BOLT | 1 ft. | GRAY DEUTSCH 6 PIN CONNECTOR (MALE) DT04-6P | 2.5( |
| RIGHT ANGLE SIDE MOUNT 4 BOLT | 1ft. | GRAY DEUTSCH 6 PIN CONNECTOR (MALE) DT04-6P | 3.00( |
| FILL TOWER SLIP OUT | 1 ft. | GRAY DEUTSCH 6 PIN CONNECTOR (MALE) DT04-6P | N/A |

CONNECTOR SPECIFICATIONS

** SERIES 2000 AIR RELIEF FITTING **

# INSTALLATION INSTRUCTIONS

FOR USE IN SEALED OR NON-VENTED TANKS ONLY

# Text boxes

THE MC AIR RELIEF FITTING WAS SPECIALLY DESIGNED TO MAINTAIN THE APPROPRIATE PRESSURE IN THE TANK.

TANKS PREVIOUSLY EQUIPPED WITH A VENT OTHER THAN MC PRODUCTS AIR RELIEF FITTING ARE STILL REQUIRED TO INSTALL THE MC AIR RELIEF FITTING WITH A MC SERIES 2000 PVC FACTORY VENTED SENSOR.

ENSURE THAT THE AIR RELIEF VALVE WILL SIT ABOVE THE FLUID LEVEL.  DRILL A 1 1/8” HOLE IN THE FILL TOWER LID.

UNSCREW THE SUPPLIED RELIEF FITTING.  INSERT ONE HALF OF THE FITTING INTO THE HOLE AND SCREW ON THE REMAINING HALF TO THE FIRST HALF HAND TIGHT.

CUT A 3 3/8” (85mm) HOLE IN THE PANEL.  SECURE THE DIAL TO THE PANEL USING THE BRACKETS AND HARDWARE AS SHOWN BELOW: