Table of contents

part one – general

G1	Definitions									G1-1

G2	Electric Utilities Act Definitions						G2-1

G3	Interpretation									G3-1

G4	Objective and Legal Nature of These Rules				G4-1

G5	ISO Authority to Change Rules						G5-1

G6	Rule Exemptions								G6-1

G7	Operation of the ISO							G7-1

G8	Limitation of Liability							G8-1

# G1	Definitions

In the ISO rules:

“10 minute clock period” means any one of the following six (6) ten (10) minute periods in any hour:

ME:01 to ME:10

ME:11 to ME:20

ME:21 to ME:30

ME:31 to ME:40

ME:41 to ME:50

ME:51 to ME:60

where “ME” means minute ending.

“abbreviated needs identification approval process” means the abbreviated needs identification approval process as contemplated in the T-Reg.

“acceptable operational reason” means with respect to an asset, any one or more of the following:

- a circumstance related to the operation of the generating asset which if it operated could reasonably be expected to affect the safety of the generating asset, the environment, personnel working at the generating asset or the public; or

- re-positioning an asset within the energy market due to the need to meet a dispatch given to that asset from the system controller to serve the stand-by ancillary services market; or

- re-positioning a generating asset within the energy market to manage physical or operational constraints associated with the asset; or

- re-positioning an importer’s or exporter’s asset within the energy market to manage physical or operational constraints associated with an interconnection or a neighbouring balancing authority; or

- a circumstance directly resulting in the generating asset not being capable of operation, which circumstance was solely caused by an occurrence of force majeure; or

- re-positioning a generating asset for electric energy that is:

- produced on the property of which a person is the owner or a tenant; and

- consumed solely by that person and solely on that property.

# “Act” means the Electric Utilities Act (Alberta), as amended from time to time.

“adequacy” means the ability of the electric system to supply the aggregate electrical demand and energy requirements of the system access customers at all times, taking into account scheduled and reasonably expected unscheduled outages of system elements.

“advance energy dispatch” means a dispatch of one or more blocks of energy for a specified future time. Advance energy dispatches are issued in anticipation of expected demand changes or to spread workload.  Under normal operating conditions, interconnected control areas do not allow changing of interchange schedules without an advance energy dispatch.

“affiliate” has the same meaning given to it in the Alberta Business Corporations Act.

“AGC unit” means a generating unit equipped for Automatic Generation Control operation.

“agent” includes:

(i)	a representative of a pool participant duly appointed and authorized by the pool participant under ISO rule 1.8 to act on behalf of and bind the pool participant with regard to transactions and other activities on the Energy Trading System and the automated dispatch and messaging system; or

(ii)	a representative of a market participant or a pool participant, as the case may be, duly appointed and authorized to act on behalf of and bind that person with regard to other ISO activities, procedures and requirements, which such appointment is made under and in accordance with the applicable ISO rules, authorizations and procedures.

“aggregation” means a collection of particulars into a whole mass or sum; total; combined.

“AIES” means Alberta’s “Interconnected Electric System” as that term is defined in the Act.

“AIES demand” means the aggregate or total, AIES demand for electric energy, including exports and associated AIES losses.

“Alberta Internal Load” (AIL) means the total energy Alberta consumes including behind-the-fence load. AIL represents the total domestic consumption of AIES connected loads in Alberta and include industrial loads served by on-site generation, and the City of Medicine Hat’s load served by the city’s generators.

“alert” means a communication issued by the system controller requesting readiness of the market participants to take urgent and timely actions to maintain the Alberta balancing authority area in a secure state with regard to energy balance. The alert also serves as information to interconnected balancing authorities regarding the increased risk of the AIES to require obligation energy and its limitations in delivering such energy to others.

“allowable dispatch variance” or “ADV” as measured from the energy market dispatch quantity (MW), means for each generating asset:

(i)	plus or minus five (5) MW for generating assets with a maximum capability of two hundred (200) MW or less, or

(ii)	plus or minus ten (10) MW for generating assets with a maximum capability of greater than two hundred (200) MW.

“ancillary service declaration” mean the ancillary service declarations identified under rule 3.6.

“ancillary service directive” means direction given to an ancillary service provider by the system controller with the understanding that the provider must comply, accepting that the facility owner retains the right and duty to take any action it deems prudent to protect the facility, its personnel, the public or the environment.

“ancillary service dispatch” means direction given to an ancillary service provider by the system controller to request the provider to supply ancillary services within those criteria agreed upon between the system controller and the ancillary service provider.

“ancillary service exchanges” means market entities for the purpose of buying and selling contracts for ancillary services.

“ancillary service merit order” means a list of all qualified ancillary service provider assets and resources for each type of ancillary service sorted in order of preference for ancillary service dispatch.

“ancillary service provider” means the pool participant holding the ancillary service dispatch rights for an asset.

“ancillary services” has the same meaning as that provided in the Act.

“applicable rules and standards” means any or all of ISO Rules, load settlement rules or reliability standards

“apparent power” means the product of the volts and amperes, comprising both real and reactive power, usually expressed in kilovoltamperes (“kVA”) or megavoltamperes (“MVA”).

“area control error” (ACE) means the instantaneous difference between actual and scheduled interchange, taking into account the effects of frequency bias, time error and unilateral inadvertent interchange if automatic correction is part of the AIES’s AGC, and a correction for metering error.

"asset" means a generating asset, load, import volume, export volume or other power pool transaction represented by an ISO identifier that enables a pool participant to submit bids, offers, operating constraints, ancillary service declarations and/or identify specific settlement information.

“asset addition form” means the form, as established by the ISO, which ISO applicants or pool participants indicate their intent to add an asset, and includes a description of that asset.

"asset marginal price" means the price in $/MWh of a pool participant's asset determined in accordance with rule 6.3.9.2.

“asset minimum off time” means the minimum time in hours, following de-synchronization that must elapse prior to accepting a dispatch to start-up and synchronize the asset to the transmission system.

“asset minimum on time” means the minimum time, in hours, which must elapse following synchronization before being able to accept a dispatch to de-synchronize the asset.

“AUC Act” means the Alberta Utilities Commission Act, as amended from time to time.

“automated dispatch and messaging system” means the software and procedures used to communicate between the system controller and market participants for real time management of the AIES.

“automatic generation control ” (AGC) means equipment that adjusts a balancing authority’s generation in a balancing authority’s area from a central location to maintain the balancing authority’s frequency or interchange schedule plus or minus frequency bias.  AGC may also accommodate automatic inadvertent payback and time error correction.

“automatic voltage regulator” (AVR) means the automatic control equipment that adjusts the excitation level of a generating unit to maintain voltage levels.

“available capability” (AC) means with respect to the following:

- for a generating asset, the maximum quantity (MW) that the generating asset is physically capable of providing during each settlement interval of the trading day.

    - for an import source asset, the maximum quantity (MW) that the importer is prepared to provide during each settlement interval of the trading day.

    - for an export sink asset, the maximum quantity (MW) that the exporter is prepared to consume  during each settlement interval of the trading day.

    - For a bid (excluding an export sink asset), the maximum quantity (MW), after accounting for any restatements to the asset’s availability to which the asset may receive an energy market dispatch in real time operations

“available capacity factor” means the percentage of time that a generating unit is available at full machine capacity.

“available transfer capability” (ATC)  means a measure of the transfer capability remaining in the physical transmission network for further commercial activity over and above already committed uses. Mathematically, ATC is defined as the total transfer capability (TTC) less the Transmission Reliability Margin (TRM), less the sum of existing transmission commitments (which includes retail customer service) and the capacity benefit margin.

“advance energy dispatch” means a dispatch of one or more blocks of energy for a specified future time. Advance energy dispatches are issued in anticipation of expected demand changes or to spread workload. Under normal operating conditions, interconnected balancing authorities do not allow changing of interchange schedules without an advance energy dispatch.

“balancing authority”  means the responsible entity that integrates resource plans ahead of time, maintains load-interchange-generation balance within a balancing authority area, and supports interconnection frequency in real time.

“balancing authority area” means  the collection of generation, transmission, and loads within the metered boundaries of the balancing authority. The balancing authority maintains load-resource balance within this area.

“balancing authority area operator” means the entity that has responsibility for maintaining a balancing authority’s  AGC functionality to ensure frequency levels and interchange are maintained per WECC standards.

“bank value” means that the power pool has sufficient funds in its bank account on the date of settlement in order to meet obligations relating to payment of funds.

“bid” means a submission made by a pool participant in accordance with rule 3.0.

“bid load” means the price responsive load bid into the ISO that can be dispatched for interruption at a set price to avoid high purchaser energy supply costs.

“billing capacity” shall have the meaning given to that term in rate schedule DTS.

“black start capability” (BSC) means the ability of a power plant or generating asset to start up without external electric supply and serve to provide power to the AIES.

“blackout” a condition where a major portion or all of the AIES is de-energized.

“block” see operating block.

“BRP” means the process developed and implemented by the ISO as a means to develop its annual business priorities and budget as well as to determine its forecast of ancillary service costs and line loss costs, which process includes an opportunity for market participants who are impacted by these costs to participate and present their case to the ISO board.

“budget” means the budget prepared by the ISO under rule 2.2.

“business day” means a day other than a Saturday, a Sunday or a statutory or non-statutory holiday in the Province of Alberta during which financial banking privileges in Alberta are suspended.

“business hours” means the normal business hours of the ISO.

“calibration factor” means an adjustment to the loss charges ensuring that the actual cost of losses is reasonably recovered through charges and credits under the ISO tariff on an annual basis.

“capacity benefit margin” (CBM) means that amount of transmission transfer capability reserved by load-serving entities with generation on the AIES up to the purchased/owned amount of transmission, to ensure access to generation from interconnected systems to meet generation reliability requirements.  CBM is currently not utilized in Alberta.

“capital contribution” means a one time payment required to be made by a system access customer for the provision of transmission facilities required for system access service.

“commercial operation” means the date upon which a load or generating unit begins to operate on the transmission system in a manner which is acceptable to the ISO and which is expected to be normal for it to so operate, after energization and commissioning.

“Commission” means the Alberta Utilities Commission established under section 2 of the Alberta Utilities Commission Act.

“Commission rules” means rules of the Commission made under the Alberta Utilities Commission Act.

“commissioning” means the process by which a facility is test, tuned and ultimately accepted for commercial operation.

“commissioning certificate” means the formal document signed by the owner of a  project being constructed under the terms of the ISO request for proposal process (or his representative) and also by representatives of ISO. The purpose of the document is to certify that all commissioning tests have been completed and accepted by the ISO, and all deficiencies have been resolved, or will be resolved by a specified date.  Any deficiencies are specifically listed.  The date indicated on this certificate marks the start of commercial operation for the facilities and thus must be very specific.

“complaint” means a submission to the ISO regarding compliance with an ISO rule by a market participant or an interested party.  A complaint must be in writing and contain, at a minimum, the following:

- The name, address, telephone number (and email address, if available) of the market participant or interested party making it;

- Whether the submission is made on a confidential basis;

- The particulars of the complaint;

- Any facts or information that support the complaint;

- The signature of the individual or authorized representative of the market participant or interested party making the complaint.

“complainant” means the market participant or interested party who submits a complaint.

“compliance monitoring audit” means a systematic and objective examination and/or testing by the ISO to monitor whether a market participant is complying with one or more applicable rules and standards.

“compressed loss factor” means the loss factors determined by applying compression to the annualized loss factors to comply with the loss factor limitations described in the T-Reg.

“confidential information” means:

- information provided to the ISO that has been specifically identified as being confidential in nature by the provider of such information; or

- information required by these rules or the ISO tariff to be kept confidential; or

- where disclosure of such information by the ISO could reasonably be expected to result in a material loss or gain to that provider; or could reasonably be expected to prejudice the provider's competitive position; or

- is financial, commercial, scientific or technical information, which if disclosed would put the supplier of the information at financial risk or competitive disadvantage.

Information is not confidential information if it is provided as a requirement of being a pool participant and identified in these rules or the ISO tariff as being required to be published by the ISO or otherwise required to be made available to others to ensure a fair, efficient and competitive market for electric energy.

“confirmation notice” is a notification from the ISO to a system access customer that the system access customer’s system access service application is complete and will be processed.

“constrained down” means, in respect of any generating unit, being directed to a lower MW output than the in merit MW output, as a result of a directive by the system controller.

“constrained on” means, in respect of a generating unit, being directed on while not in merit, as a result of a directive by the system controller.

“contingency” means an event occurring on the AIES; a “single-contingency” means the loss of a single system element under any operating condition or anticipated mode of operation.

“contingency reserve” means the reserve used to recover the area control error according to WECC criteria.

“contingency reserve obligation” to the NWPP means the provision of capacity and energy from one NWPP member to another following a contingency in accordance with NWPP guidelines.

“contract capacity” means the peak demand or supply capability (expressed in MW), as set out in the system access service agreement; it may change only in accordance with the provisions of that agreement.

“Crown” has the same meaning as that provided in the Act.

“current DDS submission” means a valid DDS offer submitted in accordance with rule 3.5.5 and includes any revision of prices and quantities in MW submitted for such DDS offer in accordance with rules 3.5.5.2 and 3.5.5.3

“current submission” means a valid offer or bid submitted in accordance with rule 3.5.1 and includes any revision submitted of prices and quantities in MW for that offer or bid in accordance with rule 3.5.3.2 b), 3.5.3.3, 3.5.4.2 b) or 3.5.4.3 .

“customer’s facilities” means all facilities interconnecting with the AIES on the system access customer’s side of the POD or POS.

“data model” means facts, figures, measurements and information pertaining to the power system. This data includes, but is not limited to, physical and electrical information associated with generators, transmission facilities and load.

“day” means the period in Alberta:

- in the case of a day on and from which time is to be one hour in advance of mountain standard time (first Sunday in April), 23 hours; or

- in the case of a day on and from which time is no longer to be one hour in advance of mountain standard time (last Sunday in October), 25 hours; and

- in all other cases, 24 hours;

beginning and ending at midnight.

“demand customers” are load system access customers and generation system access customers that consume power, the latter for the purposes of obtaining their back up supply.

“demand opportunity service” (DOS) means service under any one of rate schedules demand opportunity service (DOS 7 minutes), demand opportunity service (DOS 1 hour), demand opportunity service (DOS standard).

“Demand Transmission Service”(DTS) means service under rate schedule demand transmission service.

“Designated TFO” means with respect to a Project, the TFO or TFOs whom the ISO has determined pursuant to rule 9.1.1, to be the TFO or TFOs eligible to be issued a Direction or to whom the ISO has issued a Direction, as the case may be;

“Direction” means  where the ISO is authorized by legislation or regulation to either “direct” a TFO to assist the ISO or to do any other thing or where the ISO is authorized by the ISO rules to require a market participant to do any other thing, that the ISO has directed such TFO or market participant accordingly.

A market participant or TFO, as the case may be, to whom a direction has been delivered by the ISO may refuse to comply with such direction only if such market participant or TFO notifies the ISO that the market participant or TFO considers that

(a)   	a real and substantial risk of damage to its transmission facility or generation unit could result if the direction were complied with;

(b)   	a real and substantial risk to the safety of its employees or the public could result if the direction were complied with; or

(c)   	a real and substantial risk of undue injury to the environment could result if the direction were complied with;

“directive” means a direction given to a market participant by the system controller with the understanding that the market participant must comply, accepting that the facility owner retains the right and duty to take any action it deems prudent to protect the facility, its personnel, the public or the environment.  A directive may instruct a market participant to curtail or restore load, or to stop planned work on a transmission or generation element and restore the element to service as quickly as possible.

“direct sales agreement” has the same meaning as that provided in section 19 of the Act

“dispatch” has the same meaning as that provided in the Act, which means a direction from the ISO to a pool participant to cause, permit or alter the exchange of electric energy or ancillary services.

“dispatch down service” (DDS) means a voluntary service offered by a source asset to be dispatched off, in accordance with rule 6.3.6.

“DDS block” means the discrete MW level as identified within an offer and is the basis by which an asset receives a DDS dispatch.

“DDS dispatch” means a direction given by the system controller to a pool participant to provide DDS.

“DDS dispatched off” means a DDS dispatch has been issued for the termination of the provision of DDS.

“DDS dispatched on” means a DDS dispatch has been issued for the provision of DDS.

“DDS merit order” means a list of all valid DDS offers by DDS providers for a settlement interval consisting of DDS blocks sorted in order of price.

“DDS offer” means a submission made by a pool participant in accordance with rule 3.5.5

“dispatch log” means the permanent written or electronic record entered by the system controller that logs all dispatches and operational activities having been undertaken during a trading day.

“dispatch time” means:

- for intra-Alberta generation and load energy market dispatches, the time to start increasing or decreasing supply or demand volume (MW);

- for interconnection energy market dispatches, the interchange schedule start time;

- for ancillary service dispatches, the time when an ancillary service resource is to be in position to provide the amount (MW) of ancillary service dispatched or the time when the ancillary service is no longer required.

“dispatched off” means, when applied to bids in the energy market merit order, a dispatch has been issued for the termination of energy consumption. When applied to offers in the energy market merit order, it means a dispatch has been issued for the termination of energy delivery.

“dispatched on” means, when applied to bids in the energy market merit order, a dispatch has been issued for the consumption of electrical energy. When applied to offers in the energy market merit order, it means a dispatch has been issued for the delivery of electrical energy.

“dispute” means with respect to an ISO determination, an assertion made by a market participant to the ISO that it disagrees with such ISO determination.

“dispute submission period” means the 20 business days after the final pool statement is issued for a settlement period.

“distributor” means a party providing “distribution access service” as defined in the Act.

“disturbance” means an unplanned event which produces an abnormal system condition or the effects experienced by a power system following a contingency, such as high or low frequency, abnormal voltage, or oscillations in the system.

“disturbance control standard” (DCS) means a performance measure applied to a balancing authority (BA) or reserve sharing group (RSG) for recovering from a disturbance within 15 minutes by restoring area control error (ACE) to 0 or to its pre-disturbance level.

“DOS One (1) hour” means opportunity service to system access customers who are recallable within one (1) hour and which is provided when sufficient transmission capacity exists to accommodate the capacity scheduled for opportunity service.

“DOS request” means the document that is faxed to the system controller requesting opportunity service.

“DOS seven (7) minutes” means opportunity service to system access customers who are recallable within seven (7) minutes and which is provided when sufficient transmission capacity exists to accommodate the capacity scheduled for opportunity service.

“DOS standard” means opportunity service to system access customers which is provided when sufficient transmission capacity exists to accommodate the capacity scheduled for opportunity service.

“dynamic VArs” means reactive power that is generated or consumed by an asset as part of the asset’s inherent response during system disturbances.

“E&GI Act” means the Electricity and Gas Inspection Act (Canada) and regulations made thereunder, as amended from time to time, or such replacement legislation as may be enacted.

“electrical islands” a condition in the electrical system where geographical areas of the AIES electrically separate from the AIES, resulting from system disturbances, such that there exists both generation and load in these separated areas.

“electronic submission facilities” means the electronic facilities through which a pool participant interacts with the ISO, and as described in the pool participant manual.

“electronic tag” (e-tag) means an electronic form which contains information and data necessary for balancing authorities and other operating entities to assess, confirm, approve or deny, implement, and curtail interchange transactions as stipulated by NERC.

“eligible dispute” means a dispute that is submitted to the ISO in accordance with rule 11 by a market participant, and that is not a dispute as described at rule 11.2.

“emergency assistance” means energy provided to the party experiencing a system emergency, by the other party.

“emergency limit” means the maximum operating limit of a system element permitted by the owner of the element for a predefined duration.

“energization” means the electrical connection of the facilities to the AIES.

“energization certificate” means the formal document signed by representatives of the party requesting permission to connect transmission facilities, a load or a generator and also by representatives of the ISO. The purpose of the document is to certify that all requirements for interconnection either have been met or will be met. Any deficiencies are specifically listed.

“energy consumption” means for all pool participants

- not exporting from the AIES through use of an interconnection, the metered MWh value for the settlement interval representing the deemed electric energy received by the pool participant as recorded in the ISO data base.

- exporting from the AIES through use of an interconnection, the energy market dispatch MW volume to be transferred across that interconnection during the settlement interval and as recorded in the dispatch log.

“energy market dispatch” means a direction given by the system controller to a pool participant to cause a specified amount of electric energy to be provided to or taken off the AIES based on the energy market merit order and includes an instruction to synchronize, desynchronize, increase or decrease electrical output.

“energy market merit order” means the list of all valid offers and bids for a settlement interval sorted in order of offer and bid price blocks.

“energy market suspension” means an action which involves interrupting the normal method of calculating the system marginal price as outlined in the ISO rules, and the system controller issuing generation, load and transmission dispatches and directives in order to return the AIES to a reliable and secure state.

“energy production” means for all pool participants

- not importing to the AIES through use of an interconnection, the metered MWh value for the settlement interval representing the actual electric energy supplied by the pool participant as recorded in the ISO data base.

- importing to the AIES through use of an interconnection, the energy market dispatch MW volume to be transferred across that interconnection during the settlement interval and as recorded in the dispatch log.

“energy production uplift” means an amount that may be paid to a pool participant with a source asset that has received an energy market dispatch, subject to the conditions and calculations provided for in rule 8.1.2.

“Energy Trading System” (ETS) means the Internet-based system used to manage electricity market transactions.

“EPA approval” means the approval or approvals required under the Environmental Protection Act (Alberta) for the construction of a facility.

“EUB” means the Alberta Energy and Utilities Board established under the Alberta Energy and Utilities Board Act (Alberta).

“exception” means an error requiring special attention has occurred.  To raise an exception means the act of detection of the problem and flagging the problem for remediation whether by automated or manual means.

“export service” means service under rate schedule export service.

“exporter” means a consumer of electric energy for delivery out of Alberta.

“external referral” means a submission to the ISO regarding compliance with an ISO rule by a market participant or an interested party that does not comply with the requirements of a complaint.

“external spinning reserves” means spinning reserves obtained from a host balancing authority.

“Final Cost Report” means a document to be completed substantially in the form of the “Final Cost Report” posted by the ISO on its website;

“final statement” means the accounting statement issued pursuant to a default action in accordance with rule 8.5.1.

“financial obligations” means the power pool financial obligations of a pool participant actually incurred or likely to be incurred, including the net dollar value of the transactions plus any charges expected or to be owed to the ISO.

“financial year” means the 12 calendar month period beginning on January 1 in each year and ending on December 31 in the same year.

“firm interchange transaction” means an import or export interchange transaction for which the source balancing authority carries the associated operating reserve.

“firm load” means the load that the ISO and system members will use reasonable best efforts to supply without interruption.

“firm load responsibility” means the Alberta control area’s firm load demand served under Demand Transmission Service (DTS), plus AIES losses, plus firm export transactions, minus firm import transactions, minus that firm load under the ISO’s DTS which is under contract to provide operating reserves.

“flexible block” means a block of energy that may be partially or fully dispatched on.

“force majeure” means any occurrence which is beyond the reasonable control of the market participant, which could not have been avoided by the exercise of reasonable diligence and which prevents a market participant from performing its obligations under the ISO rules; provided that the foregoing force majeure shall not include a lack of finances or any occurrence which can be overcome by incurring reasonable additional expenses.

“forced outage” means a necessary, automatic or emergency removal of the facility directly caused by defective equipment, adverse weather, adverse environment, system condition, human element or foreign interference to avoid risk of danger or damage to personnel, the public, or physical plant.

“forced supply reduction” means a non-elective reduction in the supply of energy, including ancillary services, to an electric system or a forced extension to an outage or derate, caused by an unplanned failure of a generator or supply from another electric system, or an automatic or manual action taken to secure the electric system, or unusual or abnormal operating conditions, which results, in real time, in one of the parties lacking or being projected to lack, after drawing on all available resources, sufficient supply, including ancillary services, on its electric system to securely meet its load requirement, or obligations to WECC or MAPP.

“forecast asset marginal price” means the price of a pool participant’s asset in $/MWh determined in accordance with rule 5.2.2.

“forecast dispatch price” means the price in $/MWh calculated for each settlement interval in accordance with rule 5.2.1.

“forecast pool price” means the price in $/MWh calculated for each settlement interval in a forecast scheduling period in accordance with rule 5.3.1.

“forecast scheduling period” means the 7 day period starting with HE 1 of the next trading day and ending HE 24, of the 6th day following the next trading day.

“forward contract” has the same meaning as that provided in section 19 of the Act.

“forward market operator” means a person that provides net settlement instruction MWh volumes on behalf of pool participants, and has entered into an operating agreement with the ISO.

“generating asset” has the same meaning as generating unit as defined in the Act.

“generating asset steady state” means the state of operation that begins the first 10 minute clock period following the period in which a generating asset’s output has reached the quantity (MW) specified in an energy market dispatch, plus or minus the ADV for that generating asset.

“generating facility owner” (GFO) has the meaning as that provided for “owner” in the Act, of a generating unit.

“generating unit” has the same meaning as given in the Act.

“generating year” means the period from commercial operation to December 31 in the calendar year in which a generating asset reaches commercial operation, and the period from January 1 to December 31 in all subsequent calendar years.

“generic stacking order” means the ISO’s annual forecast of the operational dispatch of generating units and their respective operating blocks based on historical data and other information provided to the ISO expressed on a seasonal basis.

“good electric operating practice” means, in respect of a party, the standard of practice attained by exercising that degree of knowledge, skill, diligence, prudence and foresight which would reasonably and ordinarily be expected from a skilled and experienced operator engaged in the same type of undertaking under the same or similar circumstances.  Good electric operating practice is not restricted to the optimum practice or course of action to the exclusion of all others but rather comprises the spectrum of reasonable practices, methods or acts applicable to the circumstances, and having regard to economic considerations.

“governor” or “governor system” means automatic control equipment with speed droop characteristics to control generating unit speed and/or electric power output.

“gross MVAr” means 1 million VArs or 1000 kiloVArs of reactive power measured at the generating unit voltage terminals.

“gross MW”means 1 million watts or 1000 kilowatts of real power measured at the generating unit voltage terminals.

“HEEA” means the Hydro and Electric Energy Act (Alberta).

“hh” refers to the current clock hour.

“high net regulating limit” means the maximum hourly average net MW that an asset is capable of producing while performing AGC services.

“host balancing authority” means the balancing authority, outside the Alberta balancing authority, within whose metered boundaries the resources utilized by the external supplemental/spinning reserve provider to provide the spinning reserve are located.

“hour ending” or "HE" means the 60 minute period ending that hour. For example, HE 24 includes the time between 23:00 and 24:00.  For pool price and dispatch purposes, the hour starts at hh:00:00 and ends hh:59:59 for hh+1.

“import load remedial action scheme” (ILRAS) means a service provided by one or more ancillary service providers that consists of a transfer tripping scheme between the 500 kV circuit breakers at Langdon and Cranbrook on the 500 kV tie-line between Alberta and British Columbia and one or more system access customer load breakers. The remedial action scheme (RAS) is so designed that the tripping of the tie line causes the load breaker(s) to open automatically, within 8 cycles of the trip initiation of the 500 kV breaker(s).

# “import service” means service under rate schedule import service.

“importer” means an importer of electric energy to Alberta.

“in merit” means a designation applied to an asset dispatched by the system controller that qualifies the asset as eligible to set the system marginal price.

“incapability Factor” (ICBF) = 1 – available capacity factor

“inadvertent interchange” or “inadvertent energy” means the difference between the balancing authority’s net actual interchange and net interchange schedule.

“incremental loss factor” means the total increase in AIES losses experienced as a result of a specific energy transfer for a specified period of time divided by the amount of such transfer over the same period of time. “Specific energy transfer” takes into consideration locational effects.

“Independent System Operator” (ISO) has the same meaning as that provided in the Act.

“inflexible block” means a block of energy that may be dispatched on or dispatched off, but not partially dispatched on.

“interchange schedule” means the planned interchange of energy between two adjacent balancing authorities that results from the implementation of one or more interchange transaction(s).

“interchange transaction” means an energy transaction that crosses one or more control area boundaries.

“interconnected electric system” has the same meaning as that provided in the Act;

“interconnected members” means any organization external to the AIES being an owner of transmission facilities which are directly connected to facilities of the AIES.

“interconnection” means the electrical connection of the AIES with any electric system in a jurisdiction bordering Alberta.

“intermediary balancing authority area” means a balancing authority area on the interchange transaction path between the source balancing authority area and sink balancing authority area.

“internal referral” means a submission to the ISO regarding compliance with an ISO rule by the ISO board, an ISO employee or a contractor of the ISO.

“interruption” means any action causing partial or full curtailment of electrical power flow.

“intertie” has the same meaning as that provided in the T-Reg. “ISO asset list” means the list of assets as maintained by the ISO as contemplated by rule 1.3.2, which identifies current assets.

“ISO board” means members of the Independent System Operator created under section 7 (1) of the Act.

“ISO determination” means with respect to the ISO’s duties and responsibilities under the Act, the regulations under the Act or the ISO rules, a position, decision, undertaking or other action, taken by the ISO with respect to a market participant and which has been communicated to the market participant.

“ISO FDRM” means established ISO formal dispute resolution mechanisms, other than those under rule 11, available to a market participant to resolve disputes with the ISO, including but not limited to those that exist in:

a)	the ISO tariff;

b)	TFO’s tariffs; or

c)	any contract to which the ISO and the market participant are parties.

“ISO fees” means the fees established by the ISO pursuant to the Act.

“ISO load forecast” means a twenty-year load forecast for the AIES established and updated by the ISO not less than once each year.

“ISO rules” means rules made by the ISO under sections 19 and 20 of the Act.

“ISO tariff” means the tariff prepared by the ISO that has been approved by the Commission, pursuant to the Act.

“load” means the instantaneous amount of electric energy delivered or required at any specific point or points on the AIES.

“load curtailment priority” (LCP) means that priority be given to interrupting industrial and large commercial customers during supply shortfall events on a provincial basis.

“load settlement agent” (LSA) is the party conducting load settlement calculations for a particular settlement zone.

“load settlement calculations” are the calculations conducted by a load settlement agent.

“load settlement rules” means rules made by the Commission under section 24.1 of the Act.

“load settlement system” is a computer system and associated operations and interfaces operated by load settlement agents used to determine the load responsibility at each unit of the settlement interval for each retailer operating within the settlement zone.

“Load Shed Service” (LSS) means a block of load contracted by the ISO to provide instantaneous 59.5 Hz underfrequency load shedding (UFLS). The magnitude of this load will vary and will be telemetered to the ISO by the service provider.

“loss factors” means a number, expressed as a percentage, determined by the ISO:

- for each generating unit connected to the interconnected electric system, which when multiplied by the MW output of the unit reasonably represents the unit’s impact on average transmission system losses,

- for each demand opportunity service connected to the interconnected electric system, which when multiplied by the MW demand reasonably represents the service’s impact on transmission system losses,

- for each opportunity import and export transaction scheduled on the interconnected electric system, which when multiplied by the MW demand of the transaction reasonably represents the impact on transmission system losses, and

- for firm import transactions (service not currently available) scheduled on the interconnected electric system, which when multiplied by the MW demand of the transaction reasonably represents the import transaction’s impact on average transmission system losses.

“loss factor methodology” means the detailed methodology for determining loss factors set forth in Appendix 6.

“losses” means the energy that is lost through the process of transmitting electric energy.

“low net regulating limit” means the minimum hourly average net MW that an asset is capable of producing while performing AGC services.

“maneuverability” means the ability of a resource to change its real- or reactive-power output over time. Maneuverability is characterized by the ramp rate (e.g., MW/minute) of the resource and, for regulation, its acceleration rate (e.g., MW/minute2).

“MAP buyer” means the entity purchasing a MAP product from the Balancing Pool under a Balancing Pool Power Sale Agreement of December 2000 and any permitted assignee or transferee of those rights.

“MAP product” means the energy rights purchased, under a Balancing Pool Power Sale Agreement of December 2000 for the Market Achievement Plan (MAP), by a MAP buyer.

“market participant” has the same meaning as that provided in the Act.

“marketer” means an importer, an exporter, or a person trading within Alberta registering net settlement instructions.

“Market Surveillance Administrator” (MSA) has the same meaning as given in the AUC Act.

“material adverse change” means a downgrade in the credit rating of a pool participant by any credit rating agency, or an event that may result in the materially weaker creditworthiness of a pool participant as reasonably determined by the ISO.

“maximum capability” means:

- for a generating asset, the maximum quantity (MW) that the generating asset is physically capable of providing under optimal operating conditions for that asset while complying with all applicable ISO rules and terms and conditions of the ISO tariff; or

- for an import source asset, the available capability.

“maximum continuous rating” (MCR) means the maximum net power output that can be sustained by a generator.

“measurement data” is data that has been collected from meters, compensated and aggregated appropriately, and has been subjected to the required VEE checks, included in load settlement rules.

“measurement point data” is the data associated with a metered measurement point.

“measurement point definition record” is a specification that defines the physical arrangement of the metering systems as well as any algorithms used to manipulate the metering data to produce the measurement data associated with the measurement point to which the specification applies.

“mediation oversight committee” means the committee formed under rule 11.1.3.2.

“mediator” means an individual who is independent and impartial and is qualified by professional qualifications or experience to mediate a dispute under rule 11.

“merchant intertie proponent” means a person, other than the ISO, proposing an intertie.

“merchant intertie T’s and C’s” means terms and conditions that a merchant intertie proponent must file pursuant to the T-Reg.

“meter” means the apparatus which measures active energy, reactive energy or both, including any internal recorder, or clock, which is normally tested as part of the apparatus.

“meter data manager”  (MDM) means an entity responsible for collecting metering data, correcting and validating interval metering data, storing historic data, and reporting load and consumption data and corresponding time periods to appropriate parties.

“meter service provider” (MSP) means an entity that performs installation, removal, repair, and maintenance of meters.

“metered demand” means the rate at which electric energy is delivered to a POD, or from a POS, expressed in kW or MW, averaged over a 15-minute or shorter interval as deemed necessary by the ISO.

“metered energy” means the quantity of energy reflected by the relevant metering equipment as having been transferred in a particular period of time.

“metered quantity” means apparent power, reactive power, real power, time tagging and any other quantity that may be measured by metering equipment and that is required by the ISO in connection with the performance of its duties or functions under the Act.

“metering data” means the data associated with a metering point.

“metering equipment” means any current transformers, potential transformers, interconnecting wiring, meters, remote metering communication facilities and records used by the owner of the metering equipment in connection with the ISO tariff to measure metered demand.

“metering system” means a metering system is the devices required for metering a site, and the apparatus includes meter, CT/PT and communications.

“minimum stable generation” means the minimum generation level that an asset can be continuously operated at without becoming unstable.

“month” means a calendar month.

“Mountain Prevailing Time” means Mountain Standard Time when Daylight Saving Time is not in effect, and Mountain Daylight Saving Time when Daylight Saving Time is in effect.

“Mega VAr” or “MVAr” means 1 million VArs or 1000 kiloVArs of reactive power.

# “MW” means megawatt(s) or means 1 million watts or 1000 kilowatts of real electrical power.

# “MWh” means megawatt hour(s). A unit of energy.

“N minus 1” (N-1) means a single transmission outage, or the first contingency, when all other transmission lines are in service.

# “NERC” means the North American Electric Reliability Corporation.

# “net MW” means the megawatt(s) produced by an asset as measured or calculated on the high voltage side of the unit transformer.

“net settlement instruction” means a direct sales agreement or forward contract registered with the ISO by a pool participant or forward market operator under the requirements of rule 4.2, which will be netted out of meter volumes for purposes of calculating power pool settlements.

“net settlement instruction MWh volume” means net settlement instruction quantities of energy in MWh, registered with the ISO that a seller has agreed to sell or to provide a purchaser for a specified settlement interval.

“NID” means a needs identification document referred to in the T-Reg.

“NID Estimate” means a document to be completed substantially in the form of the “Needs Application Cost Estimate” posted by the ISO on its website;

“non-dispensated metering equipment” means metering equipment installed after May 31, 1998 which is not the subject of a waiver or dispensation by Industry Canada of requirements under the E&GI Act.

“non-spinning reserve” means that operating reserve not connected to the AIES but capable of serving demand within a defined period, or interruptible load that can be removed from the AIES within a defined period all in accordance with WECC criteria.

“non-zero block” means any block of energy with volume that is not 0 MW.

“normalized annual loss factor” or “Final Loss Factor” is set as the weighted average of the four seasonal shifted loss factors.

“notice of eligible dispute” has the meaning as that provided in rule 11.3.

“NWPP” means the North West Power Pool.

“off peak” means those periods of time which are not on peak.

“offer” means a submission made by a pool participant in accordance with rule 3.0.

“on peak” means the period of time from HE 9 to HE 21 inclusive, Mountain Prevailing Time during a business day.  For the BC interconnection, this means HE 0800 to HE 2300 Mountain Prevailing Time, Monday to Saturday, except for additional off-peak days identified in NERC Operating Policy 1, Appendix 1F.  For the Saskatchewan interconnection, this means HE 0700 to HE 2200 CST (no Daylight Saving Time), Monday to Saturday, except for Alberta and Saskatchewan statutory holidays as agreed by the ISO and SaskPower.  Exceptions to this definition may be used for purposes of WECC reporting, or as otherwise noted.

“open access” means providing market participants and other interested parties wishing to obtain transmission capacity on a transmission facility, the right to do so in an open and non-discriminatory manner;

“operating block” means the discrete MW level as identified within an offer or bid and is the basis by which an asset receives an energy market dispatch.

“operating constraint” means a constraint as identified in electronic submission facilities.

“operating reserves” means the capability above system demand required to provide for regulation, load forecasting errors, equipment forced and scheduled outages and local area protection.  It consists of spinning reserve and non-spinning reserve.

“operating transfer capability” (OTC) means the maximum amount of actual power that can be transferred over direct or parallel transmission elements comprising an interconnection from one balancing authority to another balancing authority, and as further defined by the WECC.

“operating week” means the period from 00:00 Saturday to 24:00 Friday.

“operational deviation” means:

- a generating asset is unable to comply with the ramping requirements set out in rule 6.6.3(a) or 6.6.3(b), or

- a generating asset operating in generating asset steady state varies outside its ADV

due to force majeure or any other circumstances related to the operation of the generating asset which could reasonably be expected to affect the available capability or safety of the generating asset, third party facilities, contracts or arrangements, the environment, personnel working at the generating asset or the public.

“opportunity capacity” means the incremental amount of transmission capacity that is available under a system access service agreement for demand opportunity service to provide capacity in addition to contract capacity for DTS.

“opportunity service” means system access service offered to any system access customer who can establish to the ISO’s satisfaction that it would not take system access service pursuant to rate schedule DTS and with respect to which, therefore, the service requirement presents the opportunity for incremental revenue with which the ISO can offset transmission costs, subject to the availability of transmission capacity.

“opportunity service customers” means those system access customers which meet the criteria for opportunity service, as defined in the ISO tariff.

“outage” means any full or partial unavailability of equipment.

“overfrequency” means the abnormal operating state or system condition that results in a system frequency above the normal 60-HERTZ.

“owner” has the same meaning as that provided in the Act;

“participation factor” means a number between 0 and 100 which describes the nature and the extent of the response of an AGC unit during a control cycle. AGC units recording participation factors from 0.1 to 100 are providing non-emergency AGC service. AGC units recording a participation factor of zero provide AGC service only during a system emergency or disturbance.

“peak metered demand waiver” refers to the process by which the ISO may, in its sole discretion, disregard the peak metered demand for a settlement period, for the purposes of calculating the billing capacity.

“physical capacity” means the maximum amount of electric power which a transmission facility, as rated by a TFO, is able to transmit.

“point of delivery”(POD) means a conceptual point of delivery from the transmission system.  A POD is the point at which energy is deemed to be delivered from the transmission system to the distribution system.  A POD is a collection of one or more interval meters (metering points) aggregated according to measurement point definition records.

“point of interconnection” (POI) means a conceptual point of exchange with non-AIES balancing authority areas at transmission voltages.  A POI is a collection of PODs and POSs aggregated according to a fixed formula to create a real or virtual point of energy delivery or receipt from outside the transmission system

“point of supply” (POS) is a conceptual point of supply onto the transmission system. A POS is the point at which energy is deemed to be supplied to the transmission system.

“pool participant” means a market participant who is registered to transact, listed in the pool participant list.

“pool participant agreement” means the form of agreement, as established by the  ISO, which a person must enter into in order to become a pool participant as contemplated by rule 1.1 and shown in Appendix 2.

“pool participant list” means the list of pool participants as maintained by the ISO as contemplated by rule 1.3.1 which identifies current pool participants and details pool participant information such as mailing locations.

“pool participant manual” means the ISO reference document that provides both technical guidance to pool participants wishing to execute ISO electronic interactions with the ISO and specific directions in using ISO sanctioned software and procedures.

“pool participation fee” means any annual participation fees determined under rule 2.2.2.

“pool price” means the price for electric energy in $/MWh reported by the ISO for each settlement interval of the trading day in accordance with rule 6.3.9.1.

“pool settlement date” means the business day on which financial settlements relating to the pool statement will occur in accordance with rule 8.4.3.

“pool statement” means the accounting statement issued pursuant to rule 8.4.

“post final adjustment mechanism” (PFAM)  is a process that market participants must follow when final settlement data is being disputed and the market participants are requesting financial adjustments be made as a result of the dispute.

# “power factor” means the ratio of real power to apparent power.

“power pool” means the power pool within the meaning of the Act.

“power purchase arrangement” (PPA) means those instruments setting forth the rights and obligations of the parties in relation to operation of generating units and entitlements to electricity and ancillary services and approved by the EUB under provisions of the Act.

“power system data” means a compilation of electrical characteristics in an integrated format representative of the physical system.

“power system monitor” means a data acquisition system that detects disturbances and stores the voltage and/or current and/or watt and/or VAr and/or frequency response information.

“power system stabilizer” (PSS) means automatic control equipment that modulates the generating unit excitation through an AVR to dampen electric power swings.

“PPA buyer” means the entity holding energy rights as acquired from the original purchase of a power purchase arrangement as contemplated in the Act, or as subsequently transferred or assigned in whole per Article 18 of the thermal power purchase arrangements.

“PPA effective date” means January 1, 2001 or such other date as the power purchase arrangements become effective.

“price block” means the discrete block identified in $/MWh for which a pool participant has placed an offer or bid within a defined MW level (see operating block).

“price responsive load” means load which, by owner discretion, may be removed or connected to the AIES as a function of the system marginal price for electricity.

“Project” means the project generally described as any one of the following:

- the means or manner by which a constraint or condition affecting the operation or performance transmission system could be alleviated as identified in a NID approved by the EUB pursuant to s. 34(3) of the Act;

- the request for system access service pursuant to s. 5(5)(b) of the TR:

- all the transmission facility proposals referred to in s. 35(1)(a) of the Act with respect to a specific approved NID; or

- the “transmission line”, as defined in the HEEA, which has been approved by the EUB pursuant to the HEEA;

“Project Change Proposal” means a document to be completed substantially in the form of the “Project Change Authorization Form” posted by the ISO on its website;

“Project Energization” means the date on which a project, including a project that is energized in stages, is fully energized and operational, as specified in an energization certificate or energization checklist of the ISO.

“Project Material” means with respect to a Project, all equipment, material and construction, installation, testing and commissioning services required for the construction of the Project and provided by a third party, but excluding any engineering services;

“Project Progress Report” means a document to be completed substantially in the form of the “Monthly Project Progress Report” posted by the ISO on its website;

“prudential requirements” means the requirements related to power pool settlement established by the ISO pursuant to rule 2.1 and as detailed in Appendix 3.

“Quarter” means each consecutive three months of a calendar year commencing January 1;

“Quarterly Projects Report” means a document to be prepared by the ISO substantially in the form of the “Quarterly Projects Report” posted by the ISO on its website;

“ramp rate” means the rate at which an asset will change its level of supply or demand in MW per minute in response to an energy market dispatch or directive.

“ramping” means the state of operation for a generating asset that begins at  the specified effective time indicated on the most current energy market dispatch  and continues until the point in time the generating asset has reached the quantity (MW) specified in the energy market dispatch, plus or minus the ADV for that generating asset.

“ratchet level” shall have the meaning ascribed thereto in rate schedule DTS.

“rated capacity” means the maximum amount of electric power which a transmission facility is rated by the manufacturer to be able to transmit.

“raw loss factor” means the loss factor calculated for each generating unit for each base case load flow condition prior to applying a shift factor or compression;

“reactive power” is the portion of electricity that establishes and sustains the electric and magnetic fields of alternating current equipment, usually expressed in kiloVArs (“kVAr”) or megaVArs (“MVAr”).

“real power” means the rate of producing, transferring, or using electrical energy, expressed in kilowatts (“kW”) or megawatts (“MW”).

“receiving balancing authority area” means the balancing authority area importing the interchange schedule.

“reference price” means the price in $/MWh calculated and determined by the ISO in accordance with rule 3.10.

“registered aggregate asset” means:

- in relation to multiple generating assets physically located at a single site, that a single offer must be submitted for the cumulative capability of the generators located at the site; or

- in relation to certain run of river hydro generation schemes that a single offer must be submitted for the cumulative capability of the registered group of generators; or

- in relation to certain generating assets or demand management processes that are operated via a single command and control scheme, that a single offer or bid must be submitted for the cumulative capability of the management scheme.

“regulated rate provider” (RRP) has the same meaning as that provided in the Act.

“regulating reserve” (RR) means the amount of spinning reserve responsive to automatic generation control that is sufficient to provide normal regulating margin.

“regulation” means the provision of generation and load response capability, including capacity, energy, and maneuverability, that responds to automatic controls issued by the system controller.

“reliability” means the combination of adequacy and system security.

“reliability compliance committee” (RCC) means the committee established by the WECC pursuant to the WECC Reliability Criteria Agreement. The responsibilities of the RCC are set out in the WECC Reliability Criteria Agreement.

“reliability management system” (RMS) means the contractual reliability management program implemented through the WECC Reliability Criteria Agreement, the WECC RMS Agreements and the Generator RMS Agreements.

“reliability standards” means “reliability standards” as defined in the T-Reg

“remedial action scheme” (RAS) means protection schemes designed to perform pre-planned corrective measures following a disturbance to provide for acceptable AIES performance or equipment protection.

“retailer” has the same meaning as that provided in the Act.

“review committee” means the committee formed under rule 11.1.3.1.

“rules” see ISO rules.

“self retailer” means a person that is a “customer” as defined in the Act, which is carrying out the functions of a retailer to obtain electricity for the customer’s own use.

“sending balancing authority area” means the balancing authority area exporting the interchange schedule

“service area” means any of the geographic areas determined by the Commission as the area of an electric distribution system pursuant to ss. 28 and 29 of the HEEA.

“Service Proposal” means a document to be completed substantially in the form of the “Proposal to Provide Service” posted by the ISO on its website;

“Service Proposal Estimate” means a document to be completed substantially in the form of the “Service Proposal Estimate” posted by the ISO on its website;

“settlement interval” means a period beginning on the hour and ending 60 minutes later and is the time increment that MWh amounts are settled financially by the ISO.  A settlement interval is the time increment at which distinct load estimates are calculated by load settlement systems.

“settlement period” means the period beginning at HE 01 on the first day of each month and ending HE 24 on the last day of the same month.

“settlement zone”  is the collection of sites that are jointly settled by a load settlement system and over which UFE is calculated and allocated.

“shift factor” means the correction that must be made to the loss factor for each individual generating unit to account for all of the MW losses in the system that are not assigned by the loss factor methodology.

“shift log” means an electronic form used by the system controller to record significant events related to the real time operation of the AIES.

“shortage of energy supply event” a state the power system may get into due to either insufficient reserves or actual shortage of energy to meet the demand.  At times such an event can be anticipated through a scheduling process, at other times it may take place due to a sudden change in load (error in the load forecast) or due to the unplanned outage of generation or transmission elements.

“signoff letter” an official ISO correspondence detailing power pool settlement dispute information including, but not limited to:

- ISO dispute number

- settlement period in dispute

- settlement summary of adjustments and pool participant signoff provision.

“sink asset” means a load, export volume or other power pool transaction represented by an ISO identifier that enables a pool participant to submit bids, operating constraints, ancillary service declarations and/or identify net settlement instruction MWh volumes bought from a seller to be settled in the power pool.

“sink balancing authority area” means the balancing authority area in which the load is located for an interchange transaction.

“site” means a unique end-use service delivery point.  This is the finest level at which load settlement recognizes retailer assignments, and receives consumption data.

“software and procedures” means any and all technical software used for ISO communications and specific directions in applying such software.

“source asset” means a generating asset, import volume, or other power pool transaction represented by an ISO identifier that enables a pool participant to submit offers, operating constraints, ancillary service declarations and/or identify net settlement instruction MWh volumes sold to a purchaser to be settled in the power pool.

“source balancing authority area” means the balancing authority area in which the generation is located for an interchange transaction.

“spinning reserve”, means the amount of unloaded generation that is synchronized to the AIES and ready to serve additional demand;

“standing offer” or “standing bid” means those offers or bids submitted in accordance with rule 3.7.

“STS Capacity” has the same meaning as in the ISO tariff.

“STS contracting party” means the party holding the STS contract for a given generating asset.  For those assets governed by a PPA, the PPA buyer will be the STS contracting party.  For other generating assets, the GFO will be the STS contracting party.

“supplemental governor response” means the ability of a governor system to respond more than that normally required for steady state asset operation.  Normal governor response ensures that the governor valves open and close in response to frequency deviations caused by normal moment to moment AIES load fluctuations.  Supplemental governor response ensures that the governor valves will move faster than normal or that governor valve movement will create a change in the electrical power output of an asset in response to a significant frequency deviation caused by a disturbance.

“supplemental reserve” means generation that is capable of being connected to the AIES and loaded within 10 minutes, or load that can be reduced within 10 minutes.

“supply shortfall directive” means a directive issued for supply shortfall energy as part of the ISO supply shortfall operating policy and procedures.

“supply shortfall energy” means a generating asset’s maximum available electric energy in excess of what is offered in operating blocks and active ancillary services, the asset is providing, which could be made available to the AIES for each settlement interval.

“Supply Transmission Service” (STS) means service under rate schedule supply transmission service.

“suspected contravention” means that the ISO, acting reasonably, and subject to rules 12.2.3, 12.3.2 and 12.4 has determined that there is some evidence to indicate a market participant has contravened applicable rules and standards.

“sustained outage” means the automatic removal of a power system element whereby attempts to restore the element by automatic means, such as automatic reclosing, fails or is not successful.

“system access customer” means a market participant who takes, or applies to take, system access service from the ISO.

“system access service” has the meaning ascribed to the term “system access service” in the Act.

“system access service agreement” means that contract, entered into between the ISO and a system access customer, which establishes the specific terms pursuant to which each individual system access customer obtains system access service.

“system average loss factor” means the losses experienced for all energy transferred during a specified period of time divided by the total of all energy transferred over the same period of time.

“system controller” means the ISO scheme to carry out the ISO duty to direct the safe, reliable and economic operation of the AIES, pursuant to the Act and includes the dispatching of the energy market merit order and the ancillary services merit order.

“System Contribution” has the same meaning as in the ISO tariff.

“system coordination plan” means the plan which the ISO provides to the TFOs and the system controller three (3) days in advance of the operating week which amalgamates all planned maintenance outages and commissioning activities that the ISO has been advised of, and which are scheduled to take place in the next operating week, and have been determined to pose an acceptable level of risk to system security from an operational planning perspective.

“system demand ramp” means the instantaneous MW to serve the sum of a) AIES load + losses plus, b) Alberta-BC interchange schedule plus, c) Alberta-Saskatchewan interchange schedule.

“system emergency” is a situation in which there is systemic equipment malfunctions, including widespread transmission or generation outages and derates, a complete loss of communication with the system controller, or a loss of the system controller’s market management tools.

“system interval meters”  are all interval meters that are defined to be part of the transmission system, and are used by the ISO in determining the energy flows of the transmission system.

“system level” is hourly values for distribution interchange, distributed generation, and border customer consumption that are needed to describe the total hourly energy flow on the AIES at the transmission level and the inputs and outputs to each and every distribution settlement zone for each hour.

“system marginal price” (SMP) means the price in $/MWh determined for each minute of a settlement interval in accordance with rule 6.3.9.2.

“system member” means any organization or individual being an owner of any or all of transmission, generation and distribution facilities.

“system security” means the safe scheduling, operation and control of the AIES on a day-to-day basis in accordance with the specified technical, security and operational standards to withstand events such as electric short circuits, unanticipated loss of AIES components and switching operations without experiencing cascading loss of AIES components or uncontrolled loss of load.

“TFO terms and conditions” means the document which sets forth the terms and conditions of service upon which the TFO will provide transmission services to the ISO.

“total trading charge” means the amount calculated pursuant to rule 2.2.3.

“total transfer capability” (TTC) means the amount of electric power that can be transferred over the interconnected transmission network in a reliable manner while meeting all of a specific set of defined pre- and post-contingency system conditions.

“trading day” means the day to which an offer or bid relates starting with HE 1 and ending HE 24.

“trading limit” means the maximum financial obligations to which a pool participant is or is expected to be owing the ISO where such limit is determined by the ISO or is the amount of financial security provided in accordance with Appendix 3.

“transmission constraint” means a limitation imposed by one or more transmission elements to normal economic merit operation of generation, load and interchange transactions or to the flow of electrical energy from one part of the AIES to the other.

“Transmission Customer” means, with respect to a specific Project, the customer, as defined in the ISO tariff, who has made application for system access service;

“transmission facility” has the same meaning as that provided in the Act.

“transmission facility owner” (TFO) has the same meaning as that provided for “owner” and “transmission facility” in the Act.

“transmission must-run” (TMR) means a generator is constrained on to operate at a minimum specified MW output level in order to maintain system security.

“Transmission Operations Coordination Committee” (TOCC) means the committee accountable to the ISO, with membership made up of transmission facility owners, charged with ongoing review and upgrading of all operating standards and guidelines for coordinated operation of the balancing authority and transmission system.

“transmission reliability margin”(TRM) means that amount of transmission transfer capability necessary to ensure that the interconnected transmission network is secure under a reasonable range of uncertainties in system conditions.

“transmission system average loss factor” means the total energy of transmission system losses divided by the total net to grid energy produced for a given calendar year for the interconnected electric system.

“transmission system losses” means, for each year, the total of the transmission system losses on the interconnected electric system.

“T-Reg” means the Transmission Regulation, as amended from time to time.

“under voltage load shed” (UVLS) means a protection scheme that enables pre-configured devices to automatically shed load to stabilize voltage when voltage falls below predetermined limits.

“underfrequency” refers to the abnormal operating state or system condition that results in a system frequency below the normal system operating frequency of 60-HERTZ.

“underfrequency load shedding” (UFLS) means the automatic or manual actions required to shed system load when the system frequency falls below the normal system operating frequency of 60-HERTZ in order to allow for the return to a secure state.

“VArs” means volt-amp reactive, a measure of reactive power.

“virtual metering point” is an effective point of measurement, that may or may not be physically locatable, where active energy or reactive energy is deemed to have been transferred through the point that is derived from one or more metering points.

“wire owner” (WO) has the meaning as that provided in the Act for “owner” and “electric distribution system”.  Wire owners maintain the responsibilities as that provided in the Act and the Roles, Relationships and Responsibilities Regulation.

“wire services provider” (WSP) is a person authorized by a wire owner to act on behalf of that owner.

“western interconnection” means the area comprising those states and provinces, or portions thereof, in western Canada, northern Mexico and the western United States in which members of the WECC operate synchronously connected transmission systems.

“WECC” means the Western Electricity Coordinating Council.

“WECC emergency assistance” means the provision of capacity and energy at the time of a system emergency by one WECC member to another as required by WECC guidelines.

"wheel-through interchange transaction" means a transaction that is represented by a single e-tag and an import offer and an export bid of equal values, that crosses two or more balancing authority area boundaries, utilizes the AIES, but does not have its associated energy consumed or produced in the AIES.

# G2	ELECTRIC UTILITIES ACT DEFINITIONS

Unless the contrary intention appears, words and phrases defined in the Act have the same meanings when used in these rules.

# G3	Interpretation

In these rules, unless the context otherwise requires:

- headings, underlining and bold italicized topic sentences are for convenience only and do not affect the interpretation of these rules;

- words referring to the singular include the plural and vice versa;

- words referring to a gender include any gender;

- all times shall be in accordance with the prevailing mountain standard or mountain daylight time in the Province of Alberta;

- words and phrases in bold type have the meanings given to them in the definitions outlined in G1.

# G4	Objective and Legal Nature of These Rules

This document sets out the ISO rules. These rules are designed to promote an efficient, fair and openly competitive market for electricity in Alberta.  All market participants are expected to comply with the Act and the rules.

The objective of these rules is to provide and promote an efficient, fair and openly competitive markets for electric energy. The ISO rules have whatever force they are given by the Act.

Each market participant is bound by and will comply with all provisions of the Act and its regulations and is subject to, and attorns to the jurisdiction of, the Courts of the Province of Alberta in respect of all matters relating to the Act, its regulations and the ISO notwithstanding the jurisdiction of incorporation or residence of the market participant.

The ISO has no obligation to connect electric services to market participants.

A person who is not a market participant will not be recognized, or entitled to any rights or benefits, under these rules, except as provided herein. A person who is a market participant but is not a pool participant may have their rights and benefits limited and their obligations extended, pursuant to the Act and the ISO rules.

# G5	ISO AUTHORITY to Change Rules

# The ISO may make rules.

The ISO may, in accordance with the Act and Commission rules, exercise its powers, from time to time as it considers desirable and appropriate to add to or change the ISO rules or remove an existing ISO rule.

The ISO will notify market participants of new ISO rules, changes to existing ISO rules or removal of existing ISO rules in accordance with the Commission rules and these ISO rules.

# G6	Rule Exemptions

This section is to be developed.

# G7	Operation of the ISO

The ISO will ensure that it is administered and operated according to these rules.

The ISO will be administered and operated in accordance with these rules and will appoint appropriate resources to ensure that systems required for the operation and administration of the ISO function properly.

The ISO will use reasonable endeavors to ensure that procedures are available respecting the use of any software, that when followed by a pool participant, will result in the pool participant entering a valid bid, offer, ancillary services declaration, operating constraint or net settlement instruction.

The ISO will give pool participants reasonable notice of any modifications that affect the use of the software.

# G8	Limitation of Liability

The ISO and certain of its related parties have a limited liability.  Market participants have certain obligations.

Pursuant to the Act, no action lies against an “Independent System Operator person” for an “Independent System Operator act” where such person is not an individual unless such act constitutes willful misconduct, negligence, or breach of contract.  Where such person is an individual, liability only accrues if such act is not carried out in good faith.  If an “Independent System Operator person” is liable to another person for an “Independent System Operator act”, then such person is liable for only direct loss or damage suffered and incurred by that other person, in accordance with the Act.

No person has any liability to another as a result of scheduling or determination of the energy market merit order, DDS merit order or the ancillary service merit order by or for the ISO, dispatch or DDS dispatch by the system controller, or a failure by the system controller to dispatch or DDS dispatch an asset, or failure of a pool participant to provide electric energy pursuant to an offer and in accordance with an energy market dispatch, or failure of pool participant to provide a service pursuant to a DDS offer and in accordance with a DDS dispatch, or a failure of a pool participant to take electric energy pursuant to a bid nor has any person any liability to another as result of the use of information made available or published through the ISO in accordance with these rules.  The obligations of the market participants are limited to:

- being bound by a bid or offer which is specified by these rules, or otherwise, to be binding and settling their accounts in accordance with these rules.  Failure to pay an account by the dates prescribed by these rules will entitle the ISO to commence legal proceedings to collect the same and to realize upon any letters of credit or other security which may have been provided;

- conducting themselves in accordance with these rules.  Failure to comply with these rules, including those with respect to settlement of accounts and in addition to the collection of such accounts, will subject the market participant to disciplinary proceedings in accordance with the rules and the obligation to comply with an ISO order pursuant to the Act.

Notwithstanding the foregoing, nothing herein prevents the ISO, the Market Surveillance Administrator or any market participant from initiating or pursuing an action or claim for non-monetary relief, such as injunction order and orders to deliver up documents, against each other or others for failure to observe these rules with respect to the disclosure of confidential information.

The foregoing is subject to the provisions of the Act, as amended or extended from time to time, and to the extent that the ISO rules are inconsistent with the Act, the latter shall prevail.

# Text boxes

Part One General