KARNATAKA POWER CORPORATION LIMITED

(A GOVERNMENT OF KARNATAKA ENTERPRISES)

MAHATHMA GANDHI HYDRO ELECTRIC POWER HOUSE

Office of the Superintending Engineer (Elec.) MGHE Works, Jog Falls: - 577 435

No. L3MGS/EL/662				                                  	     	     Date : 10.02.2016

BRIEF “e” TENDER NOTIFICATION

(‘e’ TENDER NOTIFICATION NO: KPCL/2015-16/PS/WORK_INDENT4229 DT: 09.02.2016)

- Tenders in two covers are invited through “e” Procurement Portal                                       (Website URL:https://eproc.karnataka.gov.in) for the work of “Design, Supply, Installation/Erection, Testing and commissioning of Software and Computer System for DATA acquisition and recording from existing Chartless Recorders and Digital Energy Meters/similar equipments at MGHE Power house, Jogfalls – 577 435, Sagar – Tq Shimoga - Dist, Karnataka” from reputed bidders with proven track record of successful completion of similar works.

- Tender documents can be downloaded from Government of Karnataka e-Procurement Website URL:https://eproc.karnataka.gov.in under login of bidders. After login, tender document can be downloaded from the portal within prescribed date and time published in the portal. Tenders must be electronically submitted (on-line through internet) with in the due date and time published in e-procurement portal

- Earnest Money Deposit (EMD) of Rs.41,500/-(Rupees Forty One Thousand Five Hundred Only) and tender processing fee should be paid online through e-Procurement portal using any of the payment modes like Credit Card, Direct Debit, National Electronic Fund Transfer (NEFT), Over the Counter (OTC). The tender processing fee is non-refundable.

- THE BIDDERS SHALL HAVE THE FOLLOWING PRE-QUALIFYING REQUIREMENTS:

- The Bidder shall be a regular Manufacturer/Authorized dealer/Firm and shall have proven experience in Design, Supply, Installation/Erection, Testing and commissioning of Software and Computer System for DATA acquisition and recording from existing Chartless Recorders and Digital Energy Meters in power houses/ power utilities. The bidder should have executed one work of similar nature and value not less than 07 lakhs. In proof of the above, work completion certificate copies should be furnished.

- The Bidders in the last five financial years should have achieved in at least two financial years an average annual financial turnover of Rs.20.00 lakhs. In proof Annual Report/turn over certificates duly certified by chartered accountant should be furnished.

- Bidder shall have PF registration certificate, IT-PAN No, VAT No/ Service Tax Registration certificates. In proof, PF registration, IT-PAN No, VAT No/ Service Tax Registration certificates copies shall be furnished.

- The bid of the bidders whose contracts have been terminated/ foreclosed in Karnataka Power Corporation Ltd or elsewhere during last 05 years and also those who do not meet the above prequalifying requirement will be rejected.

- The Bidders have to compulsorily visit work site ie MGHE power house, Jogfalls - 577435, KPCL, Shimoga (Dist.) before quoting to have hands on information about site conditions. The letter issued from concerned division head has to be enclosed as a proof of visiting site.

- BRIEF SCOPE OF WORK:

The brief scope of work covers Field Wiring till Recorders for the additional 32 inputs and necessary changes in the Recorders to incorporate them. Installation and Configurations of supplied PC, Monitor, Printer and Software’s. Software Programming, Networking between Existing Recorders and PC – Server and clients. Configuration of software for math functions, grouping, user defined report function, Template function, various display formats, alarms and reading data at PC. Training and hands on the supplied items and usage of Software for the M/s KPCL Engineers for 1 day. The original license software to be supplied in CD for 1000 channels/tags. Report generation configuration software shall be supplied for creation of user defined report templates.

# The firm shall demonstrate that

Configurations of all the existing recorder parameters etc. shall be Possible through remote PC. Setup/operation, replay of history and real time monitoring of the recorder parameters should be possible from any web browser through PC.

Real time monitoring & recording of recorder data shall be possible through remote PC. It possible to generate report at each scheduled time by using measured data within the recorder. Necessary report generation configuration software shall be supplied for creation of user defined report templates.

- PARTICULARS OF NOTIFICATION:

| ‘e’ Tender Notification No: KPCL/2015-16/PS/WORK_INDENT4229 Dtd: 09.02.2016 Name of work: Design, Supply, Installation/Erection, Testing and commissioning of Software and Computer System for DATA acquisition and recording from existing Chartless Recorders and Digital Energy Meters/similar equipments at MGHE Power house, Jogfalls – 577 435, Sagar – Tq Shimoga - Dist, Karnataka | Tender Inviting Authority: The Superintending Engineer (Elec.) MGHE Works, Karnataka Power Corporation Limited Jog Falls.- 577435 Sagar – Tq, Shimoga – Dist, Karnataka Ph No :08186 - 244727 Fax No :08186 - 244753 Web Site: seemghejog@gmail.com |
| --- | --- |

- BID SCHEDULE:

| 1 | Last Date & Time for on-line submission of tenders | 24.02.2016 upto 16:00 Hrs |
| --- | --- | --- |
| 2 | Date & Time of opening the Technical Bid. | On 26.02.2016 at 16:30 Hrs |
| 3 | Date & Time of opening the Financial Bid. | On 26.02.2016 at 16:45 Hrs if possible or any other convenient date which will be intimated separately. |

- Right to accept or reject any or all the tenders without assigning any reason is reserved by the undersigned.

- The bidder shall quote in Indian Rupees only. The bidder shall quote his rates including/inclusive of all the applicable taxes as per the latest GOK/GOI orders.

- The quantity of materials and work mentioned/indicated in tender may vary depending on the actual requirement at the time of placing the work order.

- The bidders who do not have independent PF(Provident Fund) registration certificate obtained from PF authorities, then such bidders if work is awarded has to remit the PF towards the labours deployed for work to KPCL contractors PF registration code.

- After evaluation of Technical Bid and whose offer meet the PQR and technical specification of the tender/bid in complete manner will be accepted and only such bidders Financial bid will be opened.

- KPCL reserves the right to verify the authenticity of any or all the certificates furnished by any or all the tenders from the authorities who have issued the same. If it is found that any of the agency/agencies have furnished false certificates/ information, the tenders submitted by them are liable for rejection.

- Further information if required can be obtained from office of the Superintending Engineer (Elec.), MGHE Works, KPCL, Jog falls – 577 435, Sagar – Tq, Shimoga – Dist, Karnataka or  HP HELPDESK 080-25501216/25501227

(R.Y.Shirali)

Superintending Engineer (Elec.),

MGHE Works, Jog Falls - 577435.

KARNATAKA POWER CORPORATION LIMITED

(A GOVERNMENT OF KARNATAKA ENTERPRISES)

Office of the Superintending Engineer (Elec.) MGHE Works, Jog Falls: - 577 435

##### ABSTRACT “e” TENDER NOTIFICATION

(‘e’ TENDER NOTIFICATION NO: KPCL/2015-16/PS/WORK_INDENT4229 DT: 09.02.2016) 30.01.2012

Bids in two covers are invited through “e” Procurement Portal                                       (Website URL:https://eproc.karnataka.gov.in) for the work of “ Design, Supply, Installation/Erection, Testing and commissioning of Software and Computer System for DATA acquisition and recording from existing Chartless Recorders and Digital Energy Meters/similar equipments at MGHE Power house, Jogfalls – 577 435, Sagar – Tq, Shimoga - Dist, Karnataka” from reputed bidders with proven track record of successful completion of similar works. Tenders must be electronically submitted (on-line through internet) within the due date and time published in e-procurement portal. Earnest Money Deposit (EMD) of Rs.41,500/- and tender processing fee should be paid online through e-Procurement portal. Last Date & Time for on-line submission of tenders is 24.02.2016 up to 16:00 Hrs. Date & Time of opening the Technical Bid is 26.02.2016 at 16:30Hrs. Further, information if required can be obtained from office of the Superintending Engineer (Elec.), MGHE Works, KPCL, Jog falls – 577 435, Sagar – Tq, Shimoga – Dist, Karnataka, Ph No: 08186-244727 or HP HELPDESK NO: 080-25501216/25501227.

(R.Y.Shirali)

Superintending Engineer (Elec.),

MGHE Works, Jog Falls - 577435.