SOHO OPERATIONAL SCRIPT

STATION KEEPING IN RMW

(Micronet 516/SOHO Server/SCRIPTS/NOMINAL OPS SCRIPTS/GENERIC SCRIPTS/SK IN RMW)

Version 14.0

Based on:	CR #G1310, Gyroless User’s Manual:  MM_SK_IN_RMW_GYROLESS

Change Record:

1.	28 Jan 99 - Added telemetry to step 1.  Changed execution profiles to 1 Hz.  Added values for nominal range of cat bed temperatures.  Added procedure to disable thruster on time standard monitoring channels, SCRF #1047.

2.	29 Jan 99 - Clarified wording in operational constraints.  Clarified wheel speed abort criteria, SCRF #1047.

3.	30 Jan 99 - Added new constraints for thruster on times for station keeping burn, SCRF #1047.

4.	1 Feb 99 - Updated maximum on time constraints, SCRF #1047.

5.	26 Feb 99 - Replaced thruster on time standard monitoring with COBS thruster monitoring function.  Added COBS Thruster Monitoring Patch uploaded as a new prerequisite.  Added note to LV A open line to verify branch pressure before opening latch valve. Added packet type 2 to the list of prerequisites.  Added additional standard monitoring channels used for SSU SEU monitoring to main activity list (#3).  Corrected discrete states for ASFD08 and ASFD18 in Step 1.  Added check for packet type 2 to Step 1.  Added hex values for terminal fields for macros, 43, 44, and 45.  Added caution to Step 4 to ensure ACU packet type 2 or 3.2 is selected before enabling thruster monitoring.  Corrected branch pressure telemetry mnemonic in Step 5.  Updated comments for ABACU201 in Step 6.  Added notes for last two abort criteria in Step 6 to send abort command without telemetry.  Added line numbers, SCRF #1104.

6.	1 Mar 99 - Corrected discrete state for ASFD18 in Step 1.  Added ACU mode relay 5 OFF and SSU based roll TM to checks in Step 1.  Added new SSU SEU monitoring to Step 3.  Added procedures called in Step 4.

7.0	27 Jul 99 - Update script with all gyroless changes from Gyroless User’s Manual, CR #G1310 - HWB.

7.1	17 Aug 99 - Added comment about time for cat bed heaters to warm up.  Changed SSU SEU to CRP flag detect as an abort criteria.  Added place to record branch A pressure after closing LV A.  Added line to adjust staircase filter to 5 after closing LV A.  Added place to log old and new values of the CRS drift.  HWB

7.2	10 Sep 99 – Added 'and enable' to description of k_rwsp_mon_strt in step 3.  Added hex values for the min and max reaction wheel speeds in step 3.  Deleted caution in step 6 stating ground reaction time is 30 minutes after FCV A switch on.  Moved statement confirming cat bed temperatures before opening FCV A in step 6.  Added check in step 10 to verify Hx has not exceeded the lowest edge prior to enabling.  Add procedure in step 15 to arm the automatic calculation of the CRS drift.

7.3	13 Sep 99 – Changed discrete state for AKSSUATM from SSU TM to SSU in step 1.  Reversed order of hex values for reaction wheel speed monitoring in step 3.  Added dump of ACU memory at address A1B0 to step 8.

8.0	22 Oct 99 – Updated values for Hx monitoring and corrective action statuses.  Reversed order of CRS drift estimation/update procedures.  Procedure a_crs_drft_est is run prior to a_crs_drft_upd.  CR 1366  HWB

9.0	20 Dec 99 – Replaced TSTOL procedure k_hx_mn_strt with a_hx_lim_upd.  Added note in step to configure SSU as roll rate anomaly detector to ensure guide star is brighter than Mv 7.  Reversed order of latch valve opening and setting reaction wheel speed monitoring limits.  Reversed order of latch valve closing and setting reaction wheel speed monitoring limits.  Added contingency action to trigger reaction wheel speed monitoring corrective action if telemetry is lost while LV A is open.  CR 1443  HWB

10.0	8 Mar 00 – Removed step prior to stationkeeping to make all stars ineligible.  Revised stationkeeping constraints.  Removed step after stationkeeping to make all stars eligible.  CR 1486  HWB

11.0	1 Dec 00 - Updated reaction wheel speed monitoring limits during maneuver to ± 3200 rpm.  CR 1575, UB44  HWB

12.0	22 Jan 01 – Updated reaction wheel speed monitoring limits during maneuver to ± 4000 rpm.  Changed procedure name to k_rwsp_mon_man to set these limits.  Updated wheel speed constraints for conducting stationkeeping burn.  CR 1599, OCD 1465, UB45 HWB.

12.1	20 Feb 01 – Removed constraint that reaction wheel speeds must be greater than 300 rpm from operational limits to begin a stationkeeping maneuver.  HWB

13.0	7 May 01 – Deleted step to clear the PROS lines.  CR 1632, UB46 HWB

14.0	27 Sep 07 – Added constraint that no burn can be < 30 msecs, disable std mon 32 during burn, changed expected state for FSPAAD = DISABLED, and added clearing of thruster cumulative on-times between burns. CR 2301, MOCR 07-0098  NJP

Positions Required:  OE, SA, CA, FDF, ESA Support Team

Prerequisites:

1.	ACU A in RMW (AKMDSACT = RMW, AKMDSCOM = COM RMW)

2.	FPSS A, SSU A, CAE A, WDE 1, 2, 3 ON and in hardware config word (AKHWCNF = 3458)

3.	LV A and B CLOSED, FCVs OFF

4.	Gyroless patches uploaded (AKMDSTMF = GYROLESS TM, KKGYRLES = GYLES.ON)

5.	Packet type 2 (AKMDSTMP = 2)

Loads:

LVA_OPEN_YYDOY

SK_RMW_YYDOY

LVA_CLOSE_YYDOY

Main Activities:

1.	Verify initial configuration

2.	Define/enable thruster monitoring

3.	Verify cat bed heaters ON

4.	Configure SSU as roll rate anomaly detector

5.	Switch ON FCV A and open LV A

6.	Define reaction wheel speed monitoring

7.	Disable Hx monitoring

8.	Dump ACU memory to monitor thruster parameters

9.	Command station keeping burn

10.	Update Hx limits

11.	Define reaction wheel speed monitoring

12.	PROS post-maneuver configuration

13.	Disable thruster monitoring

14.	Reinitialize CRS drift estimation

Plots Required:

a_rwsp_xtplot, a_rwtd_xtplot, a_thr_1to4_oti_xtplot, a_thr_5to8_oti_xtplot, a_thr_1to4_cot_xtplot, a_thr_5to8_cot_xtplot

FDF Activities:

Provide thruster on times.

Verify burn results.

Provide CRS drift estimate.

|  | Pos | Activity C’est du gateau | Procedure |
| --- | --- | --- | --- |
| 1 | FOT | STEP 1: VERIFY INITIAL CONFIGURATION |  |
| 2 |  | Verify FDE Criteria settings: ASFD06 = ENAB (CSPAAD) ASFD04 = DISAB (FSPAAD) Note: Functionality partially replaced by Std Mons 24/25 ASFD01 = DISAB (RAAD) ASFD02 = DISAB (RRAD) ASFD03 = DISAB (PAD) ASFD08 = ENAB (ARO/ESR) ASFD18 = ENAB (ARO/POWER) ASFD56 = NO ANOMALY ASFD68 = NO ARO ASFD67 = NO ESR |  |
| 3 |  | Verify AOCS configuration: AKMDSACT = RMW ASAC05A = OFF ASFPA = ON ASSSA = ON ASCAA = ON ASWD1, 2, 3 = ON AKHWCNF = h’3458’ ASLVAPOS = CLOSED ASLVBPOS = CLOSED ASFVA, B = OFF AKMDSTMP = 2 AKSSUATM = SSU |  |
| 4 |  | Verify gyroless function status: AKMDSTMF = GYROLESS TM AKGLHXFN = ENA AKSSUMON = ENA KKGYRLES = GYLES.ON KKAFES16 = ACUR.EN KKCAEI2A = ACUR.CA.EN KKAFES17 = CRP.EN KKCAEI2B = CRP.CA.EN KKAFES18 = RWS.EN KKCAEI2C = RWS.CA.EN KKAFES19 = HX.IN KKCAEI2D = HX.CA.IN KKAFES15 = THRUS.IN |  |
| 5 |  |  |  |
| 6 |  | STEP 2: DEFINE/ENABLE THRUSTER MONITORING |  |
| 7 |  | Define/enable thruster monitoring for maneuver in RMW. Thresholds: Thr 1, 2, 3, 4 1.1 sec (0000 119C) Thr 5, 6 0.3 sec (0000 04CE) Thr 7, 8 0 sec (0000 0000) Monitored over 1 format. CAUTION: Do NOT enable thruster monitoring if ACU packet type 2 or 3.2 are NOT selected. | k_thrmon_rmw Calls k_cdmu_mem_sp k_cdmu_mem_sa |
| 8 |  |  |  |
| 9 |  | STEP 3: VERIFY CAT BED HEATERS ON |  |
| 10 |  | Verify: ASCHA = ON If NOT, switch ON cat bed A heaters. Catalyst bed heaters take approximately 2 hours to warm to the nominal operating temperature, 155 degrees. | a_cbha_on |
| 11 |  |  |  |
| 12 |  | STEP 4: CONFIGURE SSU AS ROLL RATE ANOMALY DETECTOR |  |
| 13 |  | Verify/set ACU patch 5 staircase filter threshold to 5. | a_p5_stcfadj |
| 14 |  |  |  |
| 15 |  |  |  |
| 16 |  |  |  |
| 17 |  |  |  |
| 18 |  |  |  |
| 19 |  |  |  |
| 20 |  | STEP 5: FCV A ON/LV A OPEN |  |
| 21 |  | Prior to continuing, confirm cat bed temps are in nominal range (155-200 deg) |  |
| 22 |  | Power ON FCV A | a_fcva_on |
| 23 |  | Open LV A NOTE: Before opening LV A, verify PROS A branch pressure (AKPRSBPR) does not indicate a leak. LOAD NAME: LVA_OPEN_YYDDD | a_lva_open |
| 24 |  | CONTINGENCY: If telemetry is lost while LV A is OPEN, trigger reaction wheel speed monitoring corrective action by setting thresholds to 0. | k_rwspmon_trig |
| 25 |  | Disable Standard Monitoring 32 (or 30 if using RCVR-1) to prevent telemetry dropout upon transition to record in case of loss of uplink. | k_monit_dis(32) |
| 26 |  |  |  |
| 27 |  | STEP 6: DEFINE REACTION WHEEL SPEED MONITORING |  |
| 28 |  | Disable reaction wheel speed monitoring | k_rwsp_mon_stp |
| 29 |  | Set reaction wheel speed monitoring thresholds and enable: Min: -4000 rpm (hex 02EE) Max: 4000 rpm (hex 82EE) | k_rwsp_mon_man |
| 30 |  | CONTINGENCY: Until reaction wheel speed monitoring limits are reduced, continuously verify the SSU Z coordinate is “alive”. If NOT, trigger reaction wheel speed monitoring corrective action by setting thresholds to 0. | k_rwspmon_trig |
| 31 |  |  |  |
| 32 |  | STEP 7: DISABLE Hx MONITORING |  |
| 33 |  | Disable Hx monitoring to prevent unexpected ESR triggering during the maneuver | k_hx_mn_stp |
| 34 |  | STEP 8: DUMP ACU MEMORY TO MONITOR THRUSTER PARAMETERS |  |
| 35 |  | Select A1B0 as ACU memory dump address to view thruster firing parameters | /ABACU105,A1B0, 0000 |
| 36 |  | Zero out thruster accumulated on-times by starting procedure at LABEL: OTZERO (if required) | a_fcva_on at OTZERO |
| 37 |  |  |  |
| 38 |  |  |  |
| 39 |  |  |  |
| 40 |  |  |  |
| 41 |  |  |  |
| 42 |  |  |  |
| 43 |  |  |  |
| 44 |  |  |  |
| 45 |  |  |  |
| 46 |  |  |  |
| 47 |  |  |  |
| 48 |  |  |  |
| 49 |  |  |  |
| 50 |  | STEP 9: COMMAND STATION KEEPING |  |
| 51 |  | OPERATIONAL CONSTRAINTS: 1. Verify staircase filter threshold (AKSEUTH) = 5 and Z spike filter threshold (AKZFILTH) = 125 2. Transverse momentum (Ht) must always be greater than 1 Nms. 3. Minimum thruster actuation time is 30 msecs. |  |
| 52 |  | Uplink load to command station keeping. ABACU201, 000i, xxxx, yyyy, zzzz, 00C8 000j, xxxx, yyyy, zzzz, 00C8 000k, 000l, xxxx: average duty cycle is 5% (about 1 sec/20 sec - accurate on time to be defined by off modulation yyyy: Time Tag value zzzz: Repetition determined by demanded delta V 00C8: Actuation period is 20 sec +X burn: i = 3, j = 4, k = 2, l = 6. Thrusters 2 and 6 on time defined for open loop compensation. Synchronized with thrusters 3 and 4 actuation. Maximum on time to respect: < 100 ms at 14 bars and < 150 ms at 10 bars (interpolation required). Pulses grouped to increase the on time, grouping defined by integer part (maximum on time limit/equivalent on time demand per 20 sec). -X burn: i = 1, j = 2, k = 4, l = 6. Thrusters 4 and 6 on time defined for open loop compensation. Synchronized with thrusters 1 and 2 actuation. Maximum on time to respect: < 100 ms at 14 bars and < 150 ms at 10 bars (interpolation required). Pulses grouped to increase the on time, grouping defined by integer part (maximum on time limit/equivalent on time demand per 20 sec). | /load SKij_RMW_YYDOY |
| 53 |  | During burn, monitor thruster on-time, cumulated on-time, and wheel speed evolution. |  |
| 54 |  | Abort Criteria: CRP flag detect RW speed evolution (violating 190 or 4000 rpm limits) DHSS reconfiguration (send without telemetry) Loss of TM due to COMS Backup (send without telemetry) | a_inthr_abort |
| 55 |  | Verify burn results with FDF. If required, repeat step 9. |  |
| 56 |  | SKIP STEPS 10 - 15 IF ADDITIONAL THRUSTER FIRINGS ARE REQUIRED. |  |
| 57 |  | STEP 10: UPDATE Hx LIMITS |  |
| 58 |  | Update Hx limits in ACU | a_hx_lim_upd |
| 59 |  |  |  |
| 60 |  | STEP 11: DEFINE REACTION WHEEL SPEED MONITORING |  |
| 61 |  | Set reaction wheel speed monitoring thresholds to post-maneuver values: | k_rwmn_dlyadj |
| 62 |  |  |  |
| 63 |  | STEP 12: PROPULSION POST-MANEUVER CONFIGURATION |  |
| 64 |  | Close latch valve A NOTE: Before closing LV A, verify at least 25 minutes elapsed since last thruster firing PROS A branch pressure (AKPRSBPR): _____________ LOAD NAME: LVA_CLOSE_YYDOY | a_lva_close |
| 65 |  | Enable Standard Monitoring 32 (or 30 if using RCVR-1) to transition to record in case of loss of uplink. | k_ld_mon_tbl |
| 66 |  | Set staircase filter value to 5 | a_p5_stcfadj |
| 67 |  | Power OFF FCV A | a_fcva_off |
| 68 |  | Switch off CBH A | a_cbha_off |
| 69 |  |  |  |
| 70 |  |  |  |
| 71 |  | STEP 13: DISABLE THRUSTER MONITORING |  |
| 72 |  | Disable thruster monitoring | k_thrmonstop |
| 73 |  |  |  |
| 74 |  | STEP 14: REINITIALIZE CRS DRIFT ESTIMATION |  |
| 75 |  | Arm automatic calculation of CRS drift | a_crs_drft_est |
| 76 |  | Update CRS drift estimation Old Value: _____________________ New Value: _____________________ | a_crs_drft_upd |
| 77 |  |  |  |
| 78 |  |  |  |
| 79 |  |  |  |
| 80 |  |  |  |
| 81 |  |  |  |
| 82 |  |  |  |
| 83 |  |  |  |
| 84 |  |  |  |
| 85 |  |  |  |
| 86 |  |  |  |

OE Initials:                (	SA Initials:                (	CA Initials:                (