STATEMENT OF WORK

Work to be done:

To support the CND NPU (Counter Narcotics Department of the National Police of Ukraine) project a vendor is required to provide IT Equipment.

Warranty Requirements:

The vendor should also provide minimum 1 year or 2 years warranty depending on items listed in the SOW (plus additional 12 months of repairing support service) with ability to fix it locally (in Ukraine).  Contractor should verify that required IT equipment must be new, officially imported and guaranteed, with providing copy of warranty information.

Deadline: Requested items should be delivered to US Embassy in Ukraine, 4 Sikorskiy Str., 40 days term after contract signed.

Voltage, Frequency And Plug Requirements:

All devices must be compatible with standard Ukrainian voltage (220-230 volts), support 50 Hz current frequency and have C (European) or F (Schuko) plug type.

- ARTLINE WorkStation W75 v05 (W75v05) (BRAND NAME or equal)

Quantity – 5

Specifications:

| Brief specs | Minimum - Intel Core i7-8700K (3.7 - 4.7 GHz) or more RAM 16 Gb or more HDD 2 Тb + SSD 250 Гb or more nVidia Quadro P2000, 5 ГБ or more DVD-RW / LAN / without software |
| --- | --- |
| Processor (CPU) | Minimum - Six-core Intel Core i7-8700K (3.7 - 4.7 GHz) or more |
| RAM ( random access memory) | 16 Gb or more |
| Video card: | Discrete, nVidia Quadro P2000, 5 Gb or more |
| Motherboard chipset | Intel Z370 |
| HDD | HDD 2 Tb + SSD 250 Gb (M.2) |
| Power of PSU | 600 W |
| Minimum Ports | Front input/output ports: 1 x USB 3.0 connector 2 x USB 2.0 connector 2 x audio connector Rear input/output ports: 1 x PS/2 port for keyboard and mouse 1 x HDMI port 1 x DVI-D port 1 x LAN (RJ45) port 4 x USB 3.1 Type-A (Gen 1) 2 x USB 2.0/1.1 port 3 x audio connector Rear input/output ports (video card): 4 x DP 1.2 + DVI adapters |
| Cooling | Cooling CPU: Zalman CNPS10X Cooling of body (installed): 1 x 120 mm cooler |
| Pre-Installed software | No software |
| Weight | 12 kg or less |
| Minimum set includes | PC; Power cable; Documentation; Disks with drivers |
| Type of Memory | DDR4-2666 МGhz or more |
| Optical drive | DVD-RW |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Monitor Screen 23.8" Dell P2418D (210-AMPS) (BRAND NAME or equal).

Quantity - 10

Specifications:

| Display Diagonal | 23.8" or more |
| --- | --- |
| Minimum resolution | 2560 x 1440 or more |
| Matrix type | Minimum IPS |
| Matrix reaction time | 5 ms or more |
| Frequency update | 60 Ghz |
| Interface | Minimum HDMI, DisplayPort |
| Brightness | 250 cd/m² or more |
| Contrast | 1000:1 |
| Minimum features | Rotary screen (Pivot) USB Hub Height adjustment |
| Aspect ratio | 16:9 |
| Viewing angle horizontal | 178° |
| Built-in Speakers | Yes |
| Viewing angle vertical | 178° |
| VESA | 100х100 mm |
| Color | Black |
| Pixel size | 0.205 x 0.205 mm or more |
| Backlight | WLED (LED lights) |
| Number of colors | 16.7 mln or more |
| Power Consumption | In operating mode: 20W (Energy Star) / 20W (nominal) / 62W (maximum) In standby / sleep mode: less than 0.3 W |
| Minimum display adjustment options | Stand with adjustable height (130 mm) The slope (from -5 ° to + 21 °) Turn in the horizontal plane (from 45 ° to 45 °) Turn in the vertical plane (90 ° clockwise) |
| Minimum additional connectors | 1 USB 3.0 port (transmitting) 2 USB 3.0 ports (on the side panel) 2 USB 3.0 ports (on the bottom panel) |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Mouse Logitech M310 Wireless (910-003986) (BRAND NAME or equal).
Quantity – 5

Specifications:

| Source of power | 1 х AA |
| --- | --- |
| Size of mouse | Medium |
| Sensor type | Optical |
| Interface | Wireless |
| Minimum set includes | Mouse Receiver 1 battery AA type User documentation |
| Features | For both hands (symmetrical design) |
| Color | Silver or Black |
| Weight gross | 0.15 kg or less |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Keyboard Logitech K280e USB Black (920-005215) (BRAND NAME or equal)

Quantity - 5

Specifications:

| Number of buttons | 103 |
| --- | --- |
| Minimum additional functions | Waterproof Built-in wrist rest Cable length: 1.8 m |
| Interface | USB |
| Length of cable | 1.8 m or more |
| Keyboard type | Membrane |
| Features | Wrist Rest |
| OS Compatibility | Microsoft Windows |
| Minimum set includes | Packaging keyboard documentation |
| Cyrillic letters color | White, yellow or red |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

# Mobile 3G USB Modem ZTE MF821 with LTE (BRAND NAME or equal).
Quantity – 1

# Specifications:

The modem works in networks of GSM operators and supports such standards of data transmission:

# 2G - GSM 900/1800 MGHz,

# 3G - WCDMA 850/900/2100 MGHz,

# 4G - LTE 2600/2100/1800 MGHz,

| Range / frequency | LTE B3/1800 MGHz, B7/2600 MGHz |
| --- | --- |
| Standard | GSM, LTE |
| Internet connection speed | 150 Mbps (LTE) or more |
| Device type | USB modem |
| Connector for external antenna | Yes |
| Operator Support | Kyevstar, Vodafone, Lifecell, 3Mob or more |
| Mode | LTE FDD |

# Tablet Samsung Galaxy Tab S2 9.7" 2016 32GB LTE Black (SMT819NZKESEK) (BRAND NAME or equal).

# Quantity – 2

# Specifications:

| Screen view | Capacitive |
| --- | --- |
| Screen diagonal | 9.7" or more |
| RAM | 3 Gb or more |
| Minimum Wireless capabilities | Wi-Fi, Bluetooth, 3G (UMTS), 4G (LTE) |
| Built-in Memory | 32 Gb or more |
| Operating system | Android 6.0 |
| Screen resolution | 2048x1536 ore more |
| Number of Cores | Min 8 |
| Rear camera | 8 Mp or more |
| Front camera | 2.1 Mp or more |
| CPU | Qualcomm Snapdragon 652 (1.8 GHz + 1.4 GHz) platform or better version |
| Navigation System | GPS + GLONASS |
| Matrix type | Super AMOLED |
| Color | Black or gray |
| Memory card support | microSD/microSDHC |
| Memory card capacity | 128 GB or more |
| Built-in 3G module | Yes |
| SIM Cad size | Nano-Sim |
| Ability to call | Yes |
| Minimum Connectors | microUSB Connector 3.5 мм Slot for SIM-card |
| Minimum Additional characteristics | Shooting video QHD (2560x1440) 30 fps or more Fingerprint Scanner Pedometer Gyroscope Compass Light sensor |
| Battery | 5870 мА*h or more |
| Weight | 389 g or less |
| Minimum set includes | Tablet Charging device USB Cable Documents |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Laptop Dell Alienware 15 R3 (A15i716S2G16-WGR) (Brand name or equal)

Quantity – 4

Specifications:

| CPU | 4 Core Intel Core i7-7700HQ (2.8 - 3.8 GHz) platform or better version |
| --- | --- |
| Screen diagonal | Minimum 15.6" (1920x1080) Full HD |
| RAM | 16 Gb or more |
| Operating system | Windows 10 |
| Processor, GHz | 2,8 - 3,8 or more |
| Brief specifications | Screen min 15.6" IPS (1920x1080) Full HDglossy with anti-reflective coating / Minimum Intel Core i7-7700HQ (2.8 - 3.8 GHz) / RAM 16 Gb or more / HDD 1 Тb + SSD 256 Gb or more / nVidia GeForce GTX 1060, 6 Gb or more / without ОD / LAN / Wi-Fi / Bluetooth / web-camera / Windows 10 / 3.49 kg or less |
| Color | Gray or black |
| Keyboard | With illumination |
| Battery | non attachable |
| Number of slots for RAM | 2 or more |
| Weight | 3.49 kg or less |
| Type of RAM | DDR4-2400 MGHz or more |
| Minimum Additional Capabilities | Webcam Built-in microphone Built-in stereo speakers |
| Minimum graphic adapter | Discrete, nVidia GeForce GTX 1060, 6 ГБ |
| Minimum network adapters | Gigabit Ethernet Wi-Fi 802.11ac Bluetooth 4.1 |
| Minimum I / O Connectors and Ports | 3 x USB 3.0 (1 с PowerShare) / 1 x USB Type-C (совместим с Thunderbolt 3 и DisplayPort) / HDMI / mini Display Port 1.2 / LAN (RJ-45) |
| Battery Features | Lithium-ion, 8-cell, 99 W*h or more |
| Minimum set includes | Laptop Power adapter Documents |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Transcend JetFlash 790 16GB (TS16GJF790K) (brand name or equal)

Quantity – 5

Specifications:

| Memory | 16 Gb |
| --- | --- |
| Interface | USB 3.0 |
| Material | Plastic |
| Type of body | Slider |
| Minimum additional features | Encryption of data |
| Weight | 4.9 g or less |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Transcend JetFlash 790 8GB (TS8GJF790K) (brand name or equal)

Quantity – 10

Specifications:

| Memory | 8 Gb |
| --- | --- |
| Interface | USB 3.0 |
| Material | Plastic |
| Type of body | Slider |
| Additional features | Encryption of data |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

## Transcend ESD400 512GB 1.8" USB 3.0 MLC (TS512GESD400K) (brand name or equal)

Quantity – 3

Specifications:

| Memory | 512 Gb |
| --- | --- |
| Read speed | 410 Mb/s or more |
| Recording speed | 380 Mb/s or more |
| Power consumption | 5 V |
| Time to failure | 1 mln hours or more |
| Form factor | 1.8" |
| Type of memory elements | MLC NAND |
| Interface | USB |
| Drive type | External |
| Minimum set of equipment | Transcend ESD400 or equal, Case |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Hard drive Transcend StoreJet 25A3 2TB TS2TSJ25A3K 2.5 USB 3.0 External Black (brand name or equal)

Quantity - 7

Specifications:

| Memory | 2 Tb |
| --- | --- |
| Minimum Compatibility | MAC OS and Windows |
| Type of the hard drive | External |
| Form factor | 2.5" |
| Technology | HDD |
| Minimum Features | Reliable HDD |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Handheld digital scanner MSI , portable scanner (brand name or equal)

Quantity – 1

Specifications:

Paper Format А4, B4 or more Interface USB Memory card support Memory Stick OS Windows Warranty Min 2 years , required service/maintenance in Ukraine

- Printer HP LaserJet Pro M426fdw with Wi-Fi (F6W15A) + USB cable (brand name or equal)

Quantity - 2

Specifications:

| Print resolution | 600x600 dpi or more |
| --- | --- |
| Minimum Printing technology | Laser printing (b / w) |
| Type of the device | MFU |
| Image resolution of the printer / MFP | Printing: 600 x 600 dpi or more Copying: 600 x 600 dpi or more Scanning: до 1200 x 1200 dpi or more |
| Minimum Network Interfaces | Wi-Fi Ethernet |
| Duplex | Yes |
| Colors | 1 black or more |
| Paper Size and Weight | Tray 1: A4, A5, A6, B5 (JIS), 10 x 15 cm, postcards (JIS), envelopes (ISO DL, ISO C5, ISO B5); Tray 2, additional tray 3: A4, A5, A6, B5 (JIS), 10 x 15 cm, postcards (JIS), envelopes (ISO DL, ISO C5, ISO B5); Supported Media Density: Tray 1: 60 ~ 176 g / m² (up to 220 g / m² for postcards and glossy HP photo papers for color laser printing); Tray 2, additional tray 3: 60 ~ 163 g / m² (up to 176 g / m² for postcards); |
| Built-in fax | Yes |
| Print speed | Min 40 ppm or more First page output time: 5.4 seconds or less |
| LCD Monitor | 3 "color touchscreen graphic display or more |
| Printing without a computer | Printing from mobile devices |
| Supported Operating Systems | Windows versions: Windows 8 and 8.1 (32-bit and 64-bit versions), Windows 7 (32-bit and 64-bit versions), Windows Vista (32- and 64-bit versions), Windows XP (32-bit) ( SP2 and higher) Versions of Mac OS: Mac OS v10.8 Mountain Lion, v10.9 Mavericks, v10.10 Yosemite OS for mobile devices: iOS, Android, Windows 8 RT Other supported OS: Linux, RED HAT Enterprise Linux 5.0, SUSE Linux, Fedora, Ubuntu, Debian, HPUX 11 and Solaris 8/9 |
| Compatible cartridges | HP 26A Black LaserJet Toner Cartridge (~3100 p), CF226A HP 26X Black LaserJet Toner Cartridge (~9000 p), F226X1 |
| Power Consumption | 583 W (printing) or less 9.1 W (readiness) or less 2.7 W (hibernation) or less 0.7 W (when off) or less Power consumption (TEC): 1.847 kWh / h per week or less |
| Interface | 1 x USB 2.0 1 x Fast Ethernet 10 / 100Base-TX network port USB host |
| Minimum additional features | NFC Scan file format: PDF, PDF with search function, JPG, RTF, TXT, BMP, PNG, TIFF The maximum size of the scanning area (tablet): 216 x 297 mm The maximum size of the scanning area (ADF): 216 x 356 mm Scan speed (normal, A4): up to 26 ppm black and white, up to 21 ppm in color mode Copy speed (normal mode): up to 40 copies / min Processor: 1200 MHz Standard memory: 256 MB The maximum amount of memory: 256 MB Fax resolution: up to 300 x 300 dpi Transmission speed of faxes: 33.6 Kbps |
| Minimum Contents of delivery | HP LaserJet Pro M426fdn (brand name or equal) Preinstalled initial HP Laser cartridge CF226A (resource approx. 3100 pages) The accompanying documentation (hardware installation guide), software drivers and documentation on CD-ROMs Power cable Telecom cable USB Cable |
| Warranty | Min 1 year , required service/maintenance in Ukraine |

- Printer HP DesignJet T120 with Wi-Fi (CQ891B) + USB cable (brand name or equal)

Quantity – 1

Specifications:

| Print resolution | 1200x1200 dpi or more |
| --- | --- |
| Printing technology | Inkjet printing |
| Minimum Network Interfaces | Wi-Fi Ethernet |
| Number of colors | 4 or more |
| Minimum droplet size (pl) | 5.5 or more |
| Paper Size and Weight | In tray: A4, A3 Manual feed: A2, A1 In tray: 60 ~ 220 g / m² Roll / manual feed: 60 ~ 280 g / m² |
| Print speed | 40 A1 prints per hour or more |
| Print area boundaries | Roll: 5 x 5 x 5 x 5 mm Sheet: 5 x 17 x 5 x 5 mm |
| LCD Monitor | Yes |
| Printing without a computer | Yes |
| Minimum Supported Operating Systems | Microsoft Windows 7 Ultimate / Professional / Home Premium, Windows Vista Ultimate / Business / Home Premium, Windows XP (32- / 64-bit) Professional / Home, Windows Server 2008 (32- / 64-bit), Windows Server 2008 R2, Windows Server 2003 (32- / 64-bit) Mac OS X v10.6, v10.7, v10.8; Citrix XenApp; Citrix XenServer Linux |
| Compatible cartridges | Black: HP 711 Black (CZ129A) 38 ml HP 711 Black (CZ133A) 80 ml Blue: HP 711 Cyan (CZ130A) 29 ml HP 711 Cyan (CZ134A) 29 ml Magenta: HP 711 Magenta (CZ131A) 29 ml HP 711 Magenta (CZ135A) 29 ml Yellow: HP 711 Yellow (CZ132A) 29 ml HP 711 Yellow (CZ136A) 29 ml |
| Power Consumption | 35 watts maximum (in operating mode) or less 0.3 watts maximum (in standby mode) ) or less |
| Interface | High Speed USB 2.0 or more Fast Ethernet (100Base-T) |
| Minimum Contents of delivery | Printer HP Designjet T120 ePrinter (brand name or equal) Printhead Roller Initial cartridges Poster for customization Bootable software Power cable Quick reference |
| Warranty | Min 1 year , required service/maintenance in Ukraine |

- Printer Epson L805 and inks Lucky Print (brand name or equal)

Quantity – 1

Specifications:

| Number of colors (pcs) | 6 or more |
| --- | --- |
| Volume of the tank (ml) | 70 ml or more |
| Printing by technology | Inkjet |
| Min size of the drop (pl) | 1.5 |
| Printing resolution (dpi) | 5760x1440 or more |
| B / W printing speed (p/m) | 5 p/m, 37 p/m (draft) |
| Color printing speed (p/m) | 5.1 p/m, 38 p/m (draft) |
| Supported format | A4 or more |
| Media formats for printing | card, film, label, photo paper, CD / DVD, glossy paper, envelope, matte paper |
| Tray capacity (sheets) | 120 or more |
| Borderless printing | Yes |
| The ability to print without a PC (directly from the media) | Yes |
| Ability to print on discs (CD, DVD) | Yes |
| Min carrier density (g / m2) | 64 |
| Max carrier density (g / m2) | 300 |
| Interface | USB, Wi-Fi, iPrint |
| OS | OS X, Windows |
| Power, (W) | 13 or less |
| Warranty | Min 1 year , required service/maintenance in Ukraine |

- MFU Epson Workforce WF-7620 with inks (brand name or equal)

Quantity - 2

Specifications:

| Number of colors | 4 or more |
| --- | --- |
| Print format | A3+, A3 |
| Warranty | Min 12 month in Ukraine with ability to provide service in Ukraine |
| Printing without a PC | Yes |
| Connection type | Ethernet, USB, Wi-Fi |
| Printing technology | inkjet |
| Copy | Yes |
| Scanner | Yes |
| Fax | Yes |
| Printing resolution | 4800 x 2400 dpi or more |
| B / W printing speed | 39 p/m or less |
| Color printing speed | 37 p/m or less |
| Borderless printing | Yes |
| Two-sided printing | Yes |
| The minimum size of a drop | 2.8 pl or more |
| Copy resolution | 1200x2400 dpi or more |
| Copier Features | two-sided copying, scaling (25 - 400%), up to 99 copies per cycle |
| Color copying | yes |

# Photo camera Nikon 1 J5 10-30mm VR PD-Zoom Kit Black (VVA241K001) (brand name or equal)

# Quantity – 2

Specifications:

| Video recording | UHD 4K (3840x2160) or more |
| --- | --- |
| Minimum Camera Matrix | CMOS format matrix CX size 13.2 x 8.8 mm Total number of pixels: 23.01 million or more Effective number of pixels: 20.8 million or more |
| Minimum Photosensitivity | From 200 to 12 800 units in increments of 1 EV 160 ISO units; 6400 (NR); 12,800 (NR) The ability to automatically control the ISO sensitivity (160-6400, 160-3200, 160-800 ISO, user defined in P, S, A and M modes) |
| Minimum Lens | 1 Nikkor VR 10-30mm PD-Zoom Focal length 10-30 mm (equivalent to 35 mm format: 27-81 mm) The maximum aperture is f / 3.5-5.6 Minimum aperture f / 16 Lens construction: 9 elements in 7 groups (in particular, 4 aspherical elements, 1 ED glass element and HRI elements) Vibration Reduction System (VR) Lens drive: Automatic AF-S / AF-C (AF-A) mode selection, AF-AF, AF-S, AF-C, manual focus (MF) |
| Zoom | 3x or more |
| Minimum Focusing | Hybrid autofocusing (AF with phase detection / AF with contrast detection function) Auxiliary AF illuminator Focusing Area: Single-point AF: 171 focus areas; central 105 zones support AF with phase detection Auto AF area selection: 41 focus area Keeping the object |
| Minimum continuous shooting | Approx. 5, 10, 20, 30 or 60 frames per second |
| Minimum aspect ratio | NEF (RAW): 12-bit, compressed JPEG: compatible with the basic JPEG format with a high (compression of about 1: 4) or medium (compression of about 1: 8) quality level NEF (RAW) + JPEG: One photo is simultaneously recorded in NEF (RAW) and JPEG |
| Minimum Power | Rechargeable Li-ion Battery EN-EL24 (included) |
| Bolt | Electronic shutter Exposure: 1/16000 to 30 seconds in 1/3 EV increments, hand-held (maximum duration of approximately 2 minutes) |
| Minimum Exposure measurement | TTL exposure metering using a matrix Matrix, center-weighted: measured in a circle 4.5 mm in diameter at the center of the frame Spot: measured in a circle with a diameter of 2 mm for the selected focus area |
| Minimum exposure modes | P: software automatic mode with flexible program S: Shutter priority auto A: automatic aperture priority mode M: manual; automatic story selection |
| Expocorrection | From −3 to +3 EV with step 1/3 EV |
| Minimum White balance | Auto, incandescent, fluorescent light, direct sunlight, flash, cloudy sky, shadow, manual preset (for all modes except manual preset mode, fine tuning is possible) |
| Minimum Digital image effects | Pop, Retro, High contrast monochrome, Nostalgic sepia, HDR, Easy panorama, Anti-aliasing, Miniature effect, Selective color, Crossprocesses, Toy camera effect, Screen crossing, Fish eye, Skin softening |
| Self-timer | 2 s, 10 s |
| LCD Monitor | Diagonal 7.5 cm or more Type: TFT touch screen LCD with brightness adjustment Resolution: Approx. 1037 thousand points |
| Additionally | Tripod socket: 1/4 inch (ISO 1222) Picture Control System Built-in Stereo Microphone NFC support |
| Built-in flash | Controlling the i-TTL Flash Using a Matrix Synchronization with the shutter at a shutter speed of at least 1/60 s Flash mode: Auto, auto + red-eye reduction, fill flash, fill flash + slow sync, red-eye reduction, red-eye reduction + slow sync, flash with sync on rear curtain, flash with slow sync on rear curtain, off. Flash compensation: -3 to +1 EV in steps of 1/3 EV |
| Wi-Fi | Yes |
| Memory card | microSD/microSDHC microSDXC |
| Connection with PC | High-speed USB interface |
| Audio and video output | HDMI type ( D) |
| Charger | MH-31 |
| Minimum contents of delivery | Photocamera Lens 1 Nikkor VR 10–30mm PD-Zoom Rechargeable Li-ion Battery EN-EL24 Charger MH-31 Protective Cover BF-N1000 Belt AN-N1000 USB-cable UC-E20 Disk with software ViewNX 2 |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

# APC Back-UPS 1100VA IEC (BX1100LI) (brand name or equal)

# Quantity - 5

Specifications:

| Number of outlets | 6 outlets with redundant power and surge protection or more |
| --- | --- |
| Output power | 1100 VA / 550 W |
| Input voltage range when operating from a network | 150 - 280 V |
| Operating time at full load | 20 s or less |
| Battery | Built-in |
| Architecture Type | Linear Interactive |
| Operating time at half load | 6.4 min or less |
| Impulse protection, J | 273 J or more |
| LCD Display | No |
| Output waveform | Stepped Sine Wave |
| Type of battery used | Maintenance-free sealed lead-acid battery with thickened electrolyte: leakproof |
| Battery charge time, h | 6 Hours or more |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Power Extension Cable Famatel 3 м 6 sockets with a switch Green (brand name or equal)

Quantity – 5

Specifications:

| Maximum load current | 16 А |
| --- | --- |
| Number of sockets | 6 or more |
| Length of cable | 3 м or more |
| Additional features | Electrical protection: yes |
| Type of plug | C (European) plug type |
| Switch off | yes |
| Color | Green, Black or Grey |
| Warranty | Min 12 month in Ukraine |

- Shredder Fellowes 79Ci 14 sheets 3.9х38 mm 23 l (f.U4679001 / 9004)  (brand name or equal)

Quantity - 3

Specifications:

| Safety level | 4 or more |
| --- | --- |
| Number of pages to be deleted at a time | 14 or more |
| Type of cutting | Cross |
| Feed slot width | 230mm or more |
| Minimum destruction | CDs credit cards staples staples |
| Speed of destruction | 3.4 м/m or more |
| Basket capacity | 23 l or more |
| The size of the fragments | 3.9 x 38mm or more |
| Autostart / stop | Yes |
| Reverse | Yes |
| Noise level | 65 db or less |
| Warranty | Min 2 years , required service/maintenance in Ukraine |

- Server Supermicro SYS-6028R-T (brand name or equal)

Quantity - 1

Specifications:

Minimum 19" rackmount 2U

Minimum Two processors Intel Xeon E5-2600v3/v4

Minimum Chipset Intel C612

1TB memory  or more DDR4-2400 ECC

8 disks or more SAS/SATA hot-swap

Minimum 2 Ports Gigabit Ethernet (Intel i350)

IP KVM, Virtual DVD/FDD

Minimum 2 power supplies

Minimum CPU: Intel Xeon E5 16x2.1GHZ, DDR4-2400MHz, 40Mb, HT, 120W, SPEC int rate 676. Q-ty 2

Minimum RAM: 256Gb or more DDR4-2400 ECC Registered (8x32Gb fastest mode for 2 CPUs)

Minimum SATA DOM (Boot SSD): 128 Gb Supermicro SATA DOM or more. Quantity - 2

Minimum HDD: 900 Gb HDD or more Enterprise SAS 10000rpm MTBF: 2,000,000 hours, r/w: 390/335 IOps

Additional Hard Drive Trays: none

NVMe SSD in PCI-E slots: none

Minimum RAID: LSI MegaRAID 3108, 2GB cache without CacheVault, SAS 12 Gb/s, Hardware RAID: 0, 1, 2, 5, 6, 10, 50

SSD cache for LSI MegaRAID 3108, need empty hard drive trays: none

Minimum Optional network adapter: 4x1Gbit Ethernet Server Adapter, Broadcom BCM5719

FC HBA for connecting Storage/Servers: none

Minimum Power supply: Redundant

Minimum Microsoft Windows Server: Windows Server 2016 Essentials (max: 2 CPUs, 64 GB RAM,  25 users and 50 devices

Service; Standard warranty for 3 years, Base NBD for first year

22. Software Windows 10 Professional 32/64-bit, Ukrainian, 1 PC (box version) (FQC-09128) (Brand name or equal)
Quantity – 5

Specifications:

| Minimum Bits | 32- и 64-bit |
| --- | --- |
| Minimum System requirements | Processor: 1 GHz or faster RAM: 1 GB (for 32-bit systems) or 2 GB (for 64-bit systems) Hard disk space: up to 20 GB Graphic adapter supporting Microsoft DirectX 9 and WDDM driver Additional requirements for the use of certain functions: To use the touch capabilities, you need a tablet or monitor that supports multi-touch technology In order to access the Windows Store for downloading and launching applications, you need an active Internet connection, a screen resolution of at least 1024 x 768 pixels, and a Microsoft account Equipment: One license The package includes 32- and 64-bit versions on USB 3.0 media |
| Windows | Professional |
| Language | Ukrainian |
| Product type | Box version |
| Windows Edition | Windows 10 |

- Microsoft Office 2016 professional 1 PC (electronic key, All languages) (269-16801)  Brand name or equal)
Quantity - 10

Specifications:

| Products | Office 2016 or newer |
| --- | --- |
| Minimum System requirements | The processor with a clock speed of 2 GHz or higher and with support for SSE2 Memory: 1 GB RAM (for 32-bit systems); 2 GB (for 64-bit systems) Hard disk: 3 GB of free hard disk space Operating system: Windows 10, Windows 8.1, Windows 8, Windows 7 Service Pack 1 A monitor with a resolution of 1024 x 576 pixels and higher Other requirements: - Internet connection - Microsoft Account - Some features may require additional hardware or services (for more information, see http://office.microsoft.com/uk-ua/products) |
| Carrier | (diskless license kit) |
| Type of the delivery | Electronic key (Microsoft ESD) |
| Platform | MS Windows |
| Interface Languages | Multilingual |

- Antivirus McAfee LiveSafe to all user devices under the same license (1 year, electronic license) (INMCAFEELIVESAFE) for 36 month (Brand name or equal)
Quantity – 10 for 36 month

Specifications:

| Minimum system requirements | OS:Computer platforms OS Microsoft Windows 10-7 (32-bit and 64-bit), Mac OS X 10.8 or later Tablets and phones smartphones and tablets Google Android 4.0 or later. Apple iOS 8 or later Minimum Supported browsers: Internet Explorer 9.0 or later, Google Chrome, Firefox, Safari (Mac OS only) Anti-Spam software: POP3 - Windows Mail, Outlook, Netscape, IncredMail, Thunderbird, Becky, Shuriken MSN / Hotmail webmail or IMAP / POP3 email account MAPI - Outlook |
| --- | --- |
| Interface language | Russian |
| Carrier | Electronic license |
| Minimum number of users | Unlimited |
| Type | Initial Purchase |
| Product | LiveSafe |
| Product type | Electronic key |
| Validity of the license | 1 year or more |
| Minimum objects of protection | Home computers Mobile devices |
| Minimum platforms | MS Windows, MS Windows Mobile, Mac OS, Android, iOS, Linux, Symbian OS |

- Adobe Photoshop Elements и Premiere Elements 2018 Russian AOO License 1 license 1 PC (65281838AD01A00)  (Brand name or equal)
Quantity -1

Specifications:

| Type of program | Work with graphics |
| --- | --- |
| Minimum system requirements | Windows • Processor with a frequency of at least 1.6 GHz with SSE2 support • Microsoft Windows 7 with Service Pack 1, Windows 8, or Windows 10 (64-bit only) • 4 GB of RAM • 5 GB of free hard disk space for installing applications; 2 GB extra to download additional content • 1280x800 screen resolution (at 100% zoom ratio) • Audio driver and display driver compatible with Microsoft DirectX 9 or 10 • DVD-drive (for installation from DVD-ROM) • To activate the product and download content, you must have an Internet connection * Mac OS • Intel 64-bit multi-core processor • Mac OS X10.11 - macOS 10.13 • 4 GB of RAM • 5 GB of free hard disk space for installing applications; 2 GB extra to download additional content • 1280x800 screen resolution (at 100% zoom ratio) • DVD-drive (for installation from DVD-ROM) • To activate the product and download content, you must have an Internet connection * |
| Interface language | Russian |
| Carrier | PDF file that contains the key for activation |
| License type | Initial purchase |
| Product | Photoshop Elements и Premiere Elements |
| Platforms | Mac OS, MS Windows |
| Number of users | 1 PC or more |
| Validity of the license | Constant |
| Type of delivery | Electronic license |

- ABBYY FineReader 14 Standard (ESD - Electronic license)  (Brand name or equal)
Quantity – 5

Specifications:

| Minimum system requirements | PC Requirements Operating system: • Microsoft Windows 10 / 8.1 / 8/7 • Microsoft Windows Server 2016/2012/2012 R2 / 2008 R2 • To work with a localized interface, the operating system must support the appropriate language Hardware: • A PC with a clock speed of 1 GHz or higher • RAM: 1 GB (recommended: 4 GB) • Free disk space: 1.2 GB for standard installation of the program and another 1.2 GB for its optimal functioning • Video card with a resolution of at least 1024x768 pixels • An Internet connection is required to activate the serial number • Keyboard, mouse or other pointing device |
| --- | --- |
| User Type | commercial organization |
| Minimum interface language | Ukrainian, English, Bulgarian, Chinese (Simplified, Traditional), Czech, Danish, Dutch, Estonian, French, German, Greek, Hungarian, Italian, Japanese, Korean, Polish, Portuguese (Brazil), Slovak, Spanish, Swedish, Turkish, Vietnamese Note: the number of supported interface languages may differ in some local versions of ABBYY FineReader 14 |
| Product type | Electronic license |
| Edition | Standard |

- Application for automatic collection of information from websites Datacol (brand name or equal) (Brand name or equal)

Quantity – 1 for 36 month

Specifications:

#### The program greatly simplifies the user's work by automating a variety of routine tasks, monitoring and analyzing the content of the required sites, searching for and collecting contacts of potential buyers, and the like. Datacol allows you to save the data in Excel, CSV, WordPress, Blogspot, DLE or Ucoz. The program makes it possible to expand the possibilities by connecting a large number of add-ons.

Minimum Requirements:

- Automation of information search and processing

- Saving the received data in different formats

- A large number of additions

- ExpressVPN. Software that encrypts users’ web traffic and masks their IP addresses (Brand name or equal).

Quantity – 5 for 36 month

Specifications:

- Incredible VPN connection speed

- Easy-to-use VPN applications for Windows, Mac, iOS, Android, routers and Linux

- No restrictions

- Offshore Privacy Protection

- Maximum security

- 148 server locations

- Speed test

- Applications for all devices

- 24/7 chat support

- Separate tunneling

- 3G Internet Package  «Max Unlimited» (brand name or equal)

Quantity – 1 for 36 month

Specifications:

| Hight quality internet 3G | Unlimited |
| --- | --- |
| Call within Kyivstar | Unlimited |
| Calls to other carriers | 300 min |
| SMS to UA numbers | 300 SMS |

- Plotter Epson SureColor SC-T3200 with ПЗК (brand name or equal)

Quantity – 1

Specifications:

| Colors | 5 or more |
| --- | --- |
| Print format | A1+, A1 |
| Warranty | Min 12 month in Ukraine with ability to provide service in Ukraine |
| Connection type | USB, Ethernet |
| Printing technology | ink jet Epson PrecisionCore |
| Print resolution | 2880x1440 dpi or more |
| Print speed | 28 sec/А1 or more |
| Drop Size | 3.5 pl or more |
| Minimum configuration | 720x5 |
| Minimal thickness of roll material | 0.08 mm |
| Maximum thickness of roll material | 0.5 mm |
| Minimum width of roll material | 300 mm |
| Minimum length of the roll | 279 mm |
| Maximum width of roll material | 610 mm |
| Maximum diameter of roll material | 150 mm |
| Supported paper thickness | 0.08-1.5 мм |
| Supported roll size width | 300-610 mm (up to 24 inches); diameter - up to 150 mm; the thickness is 0.08-0.5 mm |
| Cable connection | USB 2.0 |
| Network connection | RJ-45 |
| LCD Display | Yes |
| OS | Windows, Mac OS |
| Noise level | 50 Db |
| Power consumption | 54 W |