SECTION A

SEE SF-1442 ATTACHED

SECTION B - SUPPLIES OR SERVICES AND PRICES/COSTS

B.1	SCOPE OF SERVICES

The Contractor shall provide personnel, supplies and equipment for all make-ready services for residences for U.S Embassy Lusaka as described in Sections B and C of this contract, and the exhibits in Section J.

B.2	TYPE OF CONTRACT

This is an indefinite-delivery, indefinite-quantity type contract for make-ready.  The Contractor shall furnish services according to task orders issued by the Contracting Officer.  Oral task orders maybe necessary for emergencies, however, they shall be issued in writing within three days after issuance of the oral instructions.  The task orders shall specify the location and type of work requested (see Section B.4 and the example in Section J, Exhibit 2).

The contract will be for a one-year period from the date of the contract award, with 4 (four) one-year options.  For each effective year of the contract, the U.S. Government guarantees a minimum order of one thousand United States dollars ($1,000.00) worth of services. The maximum amount of services ordered under each year of the contract will not exceed hundred and fifty thousand United States dollars ($150,000.00) worth of services.

B.3	PRICES/COSTS

The prices will include all work, including furnishing all labor, materials, equipment and services, unless otherwise specified in Section B.4.4.  The prices listed below shall include all labor, materials, direct and indirect costs, insurance (see FAR 52.228-3 and 52.228-5), overhead, and profit.

B.3.1   VALUE ADDED TAX

VALUE ADDED TAX (VAT).  The Government will not reimburse the Contractor for VAT under this contract.  The Contractor shall not include a line for VAT on Invoices as the U.S. Embassy has a tax exemption certificate with the host government.

### B.3.2	CURRENCY

All prices shall be in ______________________ (offeror to identify currency)

B.3.3	BASE YEAR PRICES (starting on the date stated in the Notice to Proceed and continuing for a period of 12 months)

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
| 1 | DEMOLITION SERVICES |  |  |  |  |
| 1.1 | Demolish existing concrete slab, remove debris from site and cart away to contractor's dump site(average thickness 150mm) | m³ | 7 |  |  |
| 1.2 | Demolish existing masonry wall including plaster, remove debris from site and cart away to contractor's dump site | m² | 70 |  |  |
| 1.3 | Carefully remove roof covering and all damaged purlin and roof structure, remove debris from site and cart away to contractor's dump site | m² | 60 |  |  |
| 1.4 | Remove existing gutters ,remove debris from and cart away to contractors dump site | m | 150 |  |  |
| 1.5 | Remove existing fascial board, remove debris from site and cart away to contractor’s dump site | m | 150 |  |  |
| 1.6 | Remove all existing wall tiles, remove debris from site and cart away to contractor's dump site | m | 60 |  |  |
| 1.7 | Remove all existing floor covering, remove debris from site and cart away to contractor's dump site | m² | 200 |  |  |
| 1.8 | Remove existing door frames including lintol , remove debris and hand over frame to client or cart away to contractor’s dump site | each | 15 |  |  |
| 1.9 | Remove existing window frames including lintol , remove debris and hand over frame to client or cart away to contractor's dump site | lot | 7 |  |  |
| 1.10 | Remove existing bathtub ,wash hand basin and toilet pan, clean drain and hand over to the COR | lot | 8 |  |  |
| 1.11 | Remove all plumbing piping , remove debris and cart away to contractor’s dump site | lot | 8 |  |  |
| 1.12 | Removing existing particle board/gypsum board ceiling including blundering, remove debris and cart away. | m² | 150 |  |  |
| 1.13 | Remove existing wall cabinets and hand over to the COR | lot | 7 |  |  |
| 1.14 | Remove existing curtain rails and supports. Hand over to the COR | m | 100 |  |  |
| 1.15 | Carefully remove all distribution panel boards including all cabling and take away from site | lot | 7 |  |  |
| 1.16 | Carefully remove all electrical light fittings including switches and cabling and take away from site | lot | 7 |  |  |
| 1.17 | Carefully remove all sockets including all cabling and take away from site | lot | 7 |  |  |
| 2 | CONCRETE SERVICES |  |  |  |  |
| 2.1 | Supply and cast plain concrete grade 20/20 mm aggregate. | m³ | 10 |  |  |
| 2.2 | Supply and cast vibrated reinforced concrete grade 25/20 mm aggregate. | m³ | 8 |  |  |
| 2.3 | Supply and lay deformed steel bars reinforcement (varies sizes) | kg | 100 |  |  |
| 2.4 | Supply and lay steel mesh fabric reinforcement conforce 257 allowing 200mm lap at joints | m² | 20 |  |  |
| 2.5 | Supply and lay steel mesh fabric reinforcement conforce 86 allowing 200mm lap at joints | m² | 25 |  |  |
| 2.6 | Formworks for sides of columns, steps edges of the beds | m² | 120 |  |  |
| 2.7 | Repair crack concrete screed chip off 25mm wide V joint seal with cement grout | m | 60 |  |  |
| 3 | SITE SERVICES |  |  |  |  |
| 3.1 | Clear site of works of shrubs, bushes and trees | m² | 50 |  |  |
| 3.2 | Excavate around foundation not exceeding 1m deep | m³ | 10 |  |  |
| 3.3 | Excavate to remove top soil and load and cart away to contractors tipping site average depth 150mm | m² | 70 |  |  |
| 3.4 | load and cart away surplus spoil to contractor’s dump site | m³ | 60 |  |  |
| 3.5 | Backfill and compact in layers not exceeding 150mm | m³ | 90 |  |  |
| 3.6 | Supply and install 500 gauge polythene laid under surface beds | m² | 90 |  |  |
| 3.7 | Apply approved ant termite treatment | m² | 90 |  |  |
| 4 | MASONRY SERVICES (See section C.2.11) |  |  |  |  |
| 4.1 | Erect hollow block walling (3.5N/m2 crushing strength) in cement mortar allow for brick force reinforcement every 3 courses |  |  |  |  |
| 4.1.1 | 200mm walls | m² | 60 |  |  |
| 4.1.2 | 150mm walls | m² | 80 |  |  |
| 4.1.3 | 100mm walls | m² | 70 |  |  |
| 4.2 | Erect Solid block/brick walling (5.0N/m2 crushing strength) in cement mortar and allowing for brick force reinforcement every 3 courses |  |  |  |  |
| 4.2.1 | 200mm walls | m² | 40 |  |  |
| 4.2.2 | 150mm walls | m² | 50 |  |  |
| 4.2.3 | 100mm walls | m² | 30 |  |  |
| 4.3 | Cement /sand plaster |  |  |  |  |
| 4.3.1 | Cement/sand (1:4) external rendering 20mm thick in wood float finish | m² | 100 |  |  |
| 4.3.2 | Cement/sand (1:3) internal rendering 20mm thick in steel trowelled smooth finish | m² | 100 |  |  |
| 4.3.3 | Plaster to reveal and returns | m | 100 |  |  |
| 4.4 | Beam filling between wall and roof | m | 100 |  |  |
| 4.5 | Supply and install 14g standard pressed steel door frame, double rebated including hinges, masonry, jamps and striking plate. | each | 15 |  |  |
| 4.6 | Supply and install standard metal window frame size 1200x900mm complete with handle and stays | each | 15 |  |  |
| 4.7 | Supply and install standard metal window frame size 2400x900mm complete with handle and stays | each | 8 |  |  |
| 4.8 | Supply and install standard metal window frame size 900x600mm complete with handle and stays | each | 8 |  |  |
| 4.9 | Supply and install standard metal window frame size 1800x900mm complete with handle and stays | each | 8 |  |  |
| 4.10 | Supply and apply gypsum plaster in one coat skimming finish with a steel trowel | m² | 100 |  |  |
| 4.11 | Supply and install ceramic floor tiles (Grade AAA). Including grouting and sealing. | m² | 100 |  |  |
| 4.12 | Supply and install porcelain floor tiles. (Grade AAA) including grouting and grout sealing | m² | 100 |  |  |
| 4.13 | Supply and install ceramic wall tiles(Grade AAA) including grouting and sealing | m² | 300 |  |  |
| 4.14 | Cast and install 40mm floor screed in cement/ sand mix (1:3) | m² | 150 |  |  |
| 5 | CARPENTRY SERVICES (see Section C.2.8) |  |  |  |  |
| 5.1 | Supply and install 0.5mm IBR factory painted roof sheeting including nailing and insulation | m² | 100 |  |  |
| 5.2 | Supply and install clay/cement tiles including nailing | m² | 80 |  |  |
| 5.3 | Supply and install iron roof ridge | m | 100 |  |  |
| 5.4 | Supply and install roof ridge for clay/cement tiles | m | 25 |  |  |
| 5.5 | Supply and install metal gutter | m | 100 |  |  |
| 5.6 | Supply and install PVC ceiling including edge strips | m² | 150 |  |  |
| 5.7 | Supply and install 8mm particle board ceiling | m² | 100 |  |  |
| 5.8 | Supply and install sawn 50 x 50mm softwood blandering including supports | m | 300 |  |  |
| 5.9 | Supply and install wrought softwood 225x25 mm fascias board | m | 200 |  |  |
| 5.10 | Supply and install 100mm half round PVC gutter | m | 150 |  |  |
| 5.11 | Supply and install 150mm half round PVC gutter | m | 150 |  |  |
| 5.12 | Supply and install 100mm down pipes including connection to gutter ,end outlets and wall supports | m | 60 |  |  |
| 5.13 | Supply and install standard aluminum window complete with locking, flyscreen’s and 6mm glazing. | m² | 60 |  |  |
| 5.14 | Supply and install 45mm solid core flush doors | each | 30 |  |  |
| 5.15 | Supply and install 45mm hollow core flush doors | each | 15 |  |  |
| 5.16 | Supply and install 45mm mukwa/rosewood doors | each | 30 |  |  |
| 5.17 | Supply and install 3 lever mortice lock | each | 150 |  |  |
| 5.18 | Install government supplied dead bolt locks | each | 15 |  |  |
| 5.19 | Supply and install 150 X50mm rafters including painting with preservative | m | 200 |  |  |
| 5.20 | Supply and install 100 X 38mm rafters including painting with preservative and nailing | m | 200 |  |  |
| 5.21 | Supply and install 75 X50mm purlins including painting with preservative and nailing | m | 300 |  |  |
| 5.22 | Supply and Install shelving in cabinets using 18mm block boards | m² | 80 |  |  |
| 5.23 | Supply and Install double rod wooden curtain rails including supports size 2500m | each | 50 |  |  |
| 5.24 | Supply and Install double rod metal curtain rails including supports, | each | 50 |  |  |
| 5.25 | Supply and install suspended ceiling as 10mm rhinoboard or other equal approved plasterboard with skimmed plaster fixed already existing 50x50mm branders including joint tape and cornice | m² | 150 |  |  |
| 5.26 | Replace wooden framed screen door 2000 x900mm | each | 20 |  |  |
| 5.27 | Replace aluminum framed screen door 2000 x900mm | each | 20 |  |  |
| 5.28 | Replace fly screen including frame to windows 900x600mm | each | 60 |  |  |
| 5.29 | Supply and install door stopper | each | 200 |  |  |
| 5.30 | Supply and install parquet wood floor | m² | 200 |  |  |
| 5.31 | Supply and install 400x75x20mm teak wood floor | m² | 150 |  |  |
| 5.32 | Supply and install 400x75x20mm rosewood wood floor | m² | 100 |  |  |
| 5.33 | Supply and install 100mm x 20mm wood base board | m | 400 |  |  |
| 5.34 | Supply and install 75mm softwood cornice | m | 400 |  |  |
| 5.35 | Supply and install 40mm softwood cover strips | m | 250 |  |  |
| 5.36 | Supply install 100mm butt hinges complete with screws | each | 80 |  |  |
| 5.37 | Supply and install aluminum weather strips 900mm | each | 30 |  |  |
| 5.38 | Supply and install 6mm clear glass including putty | m² | 40 |  |  |
| 5.39 | Supply and install 3mm clear glass including putty | m² | 40 |  |  |
| 5.40 | Supply and install 6mm obscure glass including putty | m² | 15 |  |  |
| 5.41 | Supply and install 3mm obscure glass including putty | m² | 15 |  |  |
| 5.42 | Check and repair sticky hinges doors, drawers and sliding doors. Per house | lot | 14 |  |  |
| 5.43 | Clean chimneys and fireplaces per house | each | 10 |  |  |
| 5.44 | Replace 30mm granite counter tops 600mm | m | 25 |  |  |
| 5.45 | Replace cabinet hinges per house | each | 14 |  |  |
| 5.46 | Repair leaky roof using roof membrane /house | lot | 10 |  |  |
| 5.47 | Replace caulking around the bathtub and kitchen sink | m | 30 |  |  |
| 5.48 | Supply and install coat hooks | each | 20 |  |  |
| 5.49 | Supply and install soap holder | each | 20 |  |  |
| 5.50 | Supply and install toilet roll holder | each | 20 |  |  |
| 5.51 | Supply and install 25mm shower curtain rod complete with end brackets. | m | 25 |  |  |
| 5.52 | Supply and install insulation in the ceiling. | m² | 150 |  |  |
| 5.53 | Supply and install 1.6mm vinyl composition tile floor 300 x300mm including supply of adhesive. | m² | 80 |  |  |
| 5.54 | Supply and replace aluminum screen materials for doors or windows | m² | 80 |  |  |
| 5.55 | Supply and replace wooden door frame complete with trims | each | 20 |  |  |
| 5.56 | Supply and install quarter round wood mouldings | m | 100 |  |  |
| 6 | PLUMBING SERVICES (see Section C.2.5) |  |  |  |  |
| 6.1 | Check and test all plumbing fixtures and snake out all interior drain lines | lot | 8 |  |  |
| 6.2 | Replace 20mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.3 | Replace 12mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.4 | Replace kitchen double bowl sink | each | 8 |  |  |
| 6.5 | Replace swing kitchen faucet Cobra or similar quality | each | 10 |  |  |
| 6.6 | Replace P trap for kitchen sink | each | 20 |  |  |
| 6.7 | Replace wash hand basin of high quality | each | 15 |  |  |
| 6.8 | Supply and replace 12mm copper/flexi connector | each | 30 |  |  |
| 6.9 | Supply and replace 20mm copper/flexi connector | each | 30 |  |  |
| 6.10 | Supply and install 20mm CPVC gate valves | each | 150 |  |  |
| 6.11 | Supply and install 12mm CPVC gate valves | each | 150 |  |  |
| 6.12 | Supply and install connection from GI to CPVC 20mm | each | 40 |  |  |
| 6.13 | Supply and install connection from GI to CPVC 12mm | each | 40 |  |  |
| 6.14 | Supply and install 40mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.15 | Supply and install 50mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.16 | Supply and install 110mm PVC pipes complete with fittings | m | 400 |  |  |
| 6.17 | Supply and install telephone bath mixer 20mm | each | 20 |  |  |
| 6.18 | Supply and install 500x500 manhole cover | each | 15 |  |  |
| 6.19 | Supply and install shower valve and mixing assembly 20mm | each | 10 |  |  |
| 6.20 | Supply and install shower head | each | 20 |  |  |
| 6.21 | Supply and install toilet pan complete with cistern | each | 25 |  |  |
| 6.22 | Supply and install seat cover | each | 25 |  |  |
| 6.23 | Supply and install WHB mixer 12mm | each | 25 |  |  |
| 6.24 | Supply and install shower cubicle 1200x900 as supplied by Make a Home with tempered glass panels or similar | each | 10 |  |  |
| 6.25 | Supply and install bathtub 1700x600x450mm deep | each | 10 |  |  |
| 6.26 | Supply and install 6mm mirror complete with dome screws and caps | each | 20 |  |  |
| 6.27 | Chisel for piping in wall 50mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.28 | Chisel for piping in slab 70mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.29 | Chisel for piping through 100mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.30 | Chisel for piping through 150mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.31 | Chisel for piping through 200mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.32 | Supply and install 100 ltrs water heater | each | 20 |  |  |
| 6.33 | Service water heater by removing accumulation of scale, clean element with vinegar and re-install | lot | 10 |  |  |
| 6.34 | Supply and install 2KW heating element complete with thermostat. | each | 20 |  |  |
| 6.35 | Install valve labels | lot | 10 |  |  |
| 6.36 | Supply and install shut off valves 20mm | lot | 10 |  |  |
| 6.37 | Remove scale from mixers | lot | 10 |  |  |
| 7 | ELECTRICAL SERVICES (see Section C.2.6) |  |  |  |  |
| 7.1 | Replace existing light switches | each | 150 |  |  |
| 7.2 | Replace existing electrical outlets | each | 250 |  |  |
| 7.3 | Replace MCBs single pole 20Amps | each | 100 |  |  |
| 7.4 | Replace MCBs single pole 10Amps | each | 100 |  |  |
| 7.5 | Replace MCBs single pole 30Amps | each | 100 |  |  |
| 7.6 | Replace MCBs single pole 40Amps | each | 100 |  |  |
| 7.7 | Replace MCBs single pole 60Amps | each | 60 |  |  |
| 7.8 | Replace MCBs single pole 80Amps | each | 60 |  |  |
| 7.9 | Replace MCBs tripple pole 20Amps | each | 20 |  |  |
| 7.10 | Replace MCBs tripple pole 60Amps | each | 20 |  |  |
| 7.11 | Replace MCBs tripple pole 80Amps | each | 20 |  |  |
| 7.12 | Supply and install 1.5mm 2 cable red | m | 4000 |  |  |
| 7.13 | Supply and install 2.5mm 2 cable red | m | 4000 |  |  |
| 7.14 | Supply and install 4mm 2 cable red | m | 2500 |  |  |
| 7.15 | Supply and install 6mm 2 cable red | m | 1000 |  |  |
| 7.16 | supply and install 4 ft single fluorescent light fitting | each | 200 |  |  |
| 7.17 | supply and install 2 ft single fluorescent light fitting | each | 20 |  |  |
| 7.18 | supply and install 4 ft double fluorescent light fitting | each | 200 |  |  |
| 7.19 | supply and install 2 ft double fluorescent light fitting | each | 20 |  |  |
| 7.20 | supply and install recessed vapor barrier light fixture | each | 80 |  |  |
| 7.21 | Supply and install 6" spherical light fitting | each | 80 |  |  |
| 7.22 | Supply and install 8" spherical light fitting | each | 80 |  |  |
| 7.23 | Install government supplied chandelier | each | 20 |  |  |
| 7.24 | Install government supplied ceiling fan | each | 30 |  |  |
| 7.25 | Install government supplied GFCI socket outlets | each | 30 |  |  |
| 7.26 | Install government supplied door bell | each | 15 |  |  |
| 7.27 | Supply and install 20mm PVC electrical conduits | m | 1000 |  |  |
| 7.28 | Supply and install 25mm PVC electrical conduits | m | 1000 |  |  |
| 7.29 | Supply and install metal boxes 3"x3" | each | 300 |  |  |
| 7.30 | Supply and install metal boxes 6"x3" | each | 300 |  |  |
| 7.31 | Supply and install junction boxes complete with covers | each | 300 |  |  |
| 7.32 | Replace geyser switches | each | 30 |  |  |
| 7.33 | Supply and install light bulbs | each | 300 |  |  |
| 7.34 | supply and install lightening arrestors | each | 60 |  |  |
| 7.35 | Label distribution panel | lot | 10 |  |  |
| 7.36 | Install dead front panel | lot | 10 |  |  |
| 8 | PAINTING SERVICES (See Section C.2.1.4) |  |  |  |  |
| 8.1 | Clean old paint, repair plaster, prime and smooth surface, apply (1) coat of interior undercoat paint to walls and ceiling | m² | 2500 |  |  |
| 8.2 | Colored painting walls, two coats, (semi-gloss) paint, no surface preparation | m² | 4000 |  |  |
| 8.3 | Painting ceilings, two coats, (PVA) paint, no surface preparation | m² | 3000 |  |  |
| 8.4 | Paint, exterior oil 2 coat | m² | 800 |  |  |
| 8.5 | Paint, exterior latex, 2coat | m² | 2000 |  |  |
| 8.6 | Paint, exterior enamel,2coats | m² | 1000 |  |  |
| 8.7 | Paint, interior latex, 2 coat | m² | 2000 |  |  |
| 8.8 | Painting trim/baseboards, one coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.9 | Varnishing of woodwork, following surface preparation | m² | 1000 |  |  |
| 8.10 | Textured Surfaces preparatory work | m² | 1000 |  |  |
| 8.11 | Painting of textured surfaces, one coat, (latex semi-gloss, spray application incl. Floor coverings, etc.) | m² | 1000 |  |  |
| 8.12 | Prepare surface and apply ceiling texture (spray application incl. Floor coverings, etc.) | m² | 600 |  |  |
| 8.13 | Painting wood surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 600 |  |  |
| 8.14 | Painting metal surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 200 |  |  |
| 8.15 | Painting wood surfaces( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.16 | Painting metal surfaces ( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 9 | HVAC SERVICES (see Section C.2.7) |  |  |  |  |
| 9.1 | Install indoor Evaporator units. | each | 40 |  |  |
| 9.2 | Install outside condensing units | each | 40 |  |  |
| 9.3 | Install refrigeration lines/pipes between the inside and outside units. The refrigeration lines/pipes between the inside and outside units must be installed following a route and in a manner acceptable to the Contracting Officer Representative. Insulate all pipes with Armaflex | each | 40 |  |  |
| 9.4 | Install all pipes in Trunkings and provide for Air-conditioning drain. | each | 40 |  |  |
| 9.5 | Install thermostat holder. The location where the thermostat will be installed will be coordinated with the contracting Officer Representative. | each | 40 |  |  |
| 9.6 | Provide for an Isolation switch for the indoor and outdoor unit | each | 40 |  |  |
| 9.7 | Install electrical power and signal cable between indoor and outdoor unit. | each | 40 |  |  |
| 9.8 | The new AC units must be tested for proper operation. The contractor must demonstrate to the Contracting Officer Representatives that the system functions properly before the project will be accepted. | each | 40 |  |  |
| 9.9 | Carry out full service of the existing ACs as described in C.2.4 (c ) | each | 40 |  |  |
|  | Total of all line-item prices: |  |  |  |  |
|  | Base year total |  |  |  |  |

*m² – square meter

The estimated amounts are based on total estimated Government requirements.  This means that if more than one award is made, the estimated amount of work awarded under task order(s) to any single contractor will be less than the amount shown.

B.3.4	FIRST OPTION YEAR PRICES

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
| 1 | DEMOLITION SERVICES |  |  |  |  |
| 1.1 | Demolish existing concrete slab, remove debris from site and cart away to contractor's dump site(average thickness 150mm) | m³ | 7 |  |  |
| 1.2 | Demolish existing masonry wall including plaster, remove debris from site and cart away to contractor's dump site | m² | 70 |  |  |
| 1.3 | Carefully remove roof covering and all damaged purlin and roof structure, remove debris from site and cart away to contractor's dump site | m² | 60 |  |  |
| 1.4 | Remove existing gutters ,remove debris from and cart away to contractors dump site | m | 150 |  |  |
| 1.5 | Remove existing fascial board, remove debris from site and cart away to contractor’s dump site | m | 150 |  |  |
| 1.6 | Remove all existing wall tiles, remove debris from site and cart away to contractor's dump site | m | 60 |  |  |
| 1.7 | Remove all existing floor covering, remove debris from site and cart away to contractor's dump site | m² | 200 |  |  |
| 1.8 | Remove existing door frames including lintol , remove debris and hand over frame to client or cart away to contractor’s dump site | each | 15 |  |  |
| 1.9 | Remove existing window frames including lintol , remove debris and hand over frame to client or cart away to contractor's dump site | lot | 7 |  |  |
| 1.10 | Remove existing bathtub ,wash hand basin and toilet pan, clean drain and hand over to the COR | lot | 8 |  |  |
| 1.11 | Remove all plumbing piping , remove debris and cart away to contractor’s dump site | lot | 8 |  |  |
| 1.12 | Removing existing particle board/gypsum board ceiling including blundering, remove debris and cart away. | m² | 150 |  |  |
| 1.13 | Remove existing wall cabinets and hand over to the COR | lot | 7 |  |  |
| 1.14 | Remove existing curtain rails and supports. Hand over to the COR | m | 100 |  |  |
| 1.15 | Carefully remove all distribution panel boards including all cabling and take away from site | lot | 7 |  |  |
| 1.16 | Carefully remove all electrical light fittings including switches and cabling and take away from site | lot | 7 |  |  |
| 1.17 | Carefully remove all sockets including all cabling and take away from site | lot | 7 |  |  |
| 2 | CONCRETE SERVICES |  |  |  |  |
| 2.1 | Supply and cast plain concrete grade 20/20 mm aggregate. | m³ | 10 |  |  |
| 2.2 | Supply and cast vibrated reinforced concrete grade 25/20 mm aggregate. | m³ | 8 |  |  |
| 2.3 | Supply and lay deformed steel bars reinforcement (varies sizes) | kg | 100 |  |  |
| 2.4 | Supply and lay steel mesh fabric reinforcement conforce 257 allowing 200mm lap at joints | m² | 20 |  |  |
| 2.5 | Supply and lay steel mesh fabric reinforcement conforce 86 allowing 200mm lap at joints | m² | 25 |  |  |
| 2.6 | Formworks for sides of columns, steps edges of the beds | m² | 120 |  |  |
| 2.7 | Repair crack concrete screed chip off 25mm wide V joint seal with cement grout | m | 60 |  |  |
| 3 | SITE SERVICES |  |  |  |  |
| 3.1 | Clear site of works of shrubs, bushes and trees | m² | 50 |  |  |
| 3.2 | Excavate around foundation not exceeding 1m deep | m³ | 10 |  |  |
| 3.3 | Excavate to remove top soil and load and cart away to contractors tipping site average depth 150mm | m² | 70 |  |  |
| 3.4 | load and cart away surplus spoil to contractor’s dump site | m³ | 60 |  |  |
| 3.5 | Backfill and compact in layers not exceeding 150mm | m³ | 90 |  |  |
| 3.6 | Supply and install 500 gauge polythene laid under surface beds | m² | 90 |  |  |
| 3.7 | Apply approved ant termite treatment | m² | 90 |  |  |
| 4 | MASONRY SERVICES (See section C.2.11) |  |  |  |  |
| 4.1 | Erect hollow block walling (3.5N/m2 crushing strength) in cement mortar allow for brick force reinforcement every 3 courses |  |  |  |  |
| 4.1.1 | 200mm walls | m² | 60 |  |  |
| 4.1.2 | 150mm walls | m² | 80 |  |  |
| 4.1.3 | 100mm walls | m² | 70 |  |  |
| 4.2 | Erect Solid block/brick walling (5.0N/m2 crushing strength) in cement mortar and allowing for brick force reinforcement every 3 courses |  |  |  |  |
| 4.2.1 | 200mm walls | m² | 40 |  |  |
| 4.2.2 | 150mm walls | m² | 50 |  |  |
| 4.2.3 | 100mm walls | m² | 30 |  |  |
| 4.3 | Cement /sand plaster |  |  |  |  |
| 4.3.1 | Cement/sand (1:4) external rendering 20mm thick in wood float finish | m² | 100 |  |  |
| 4.3.2 | Cement/sand (1:3) internal rendering 20mm thick in steel trowelled smooth finish | m² | 100 |  |  |
| 4.3.3 | Plaster to reveal and returns | m | 100 |  |  |
| 4.4 | Beam filling between wall and roof | m | 100 |  |  |
| 4.5 | Supply and install 14g standard pressed steel door frame, double rebated including hinges, masonry, jamps and striking plate. | each | 15 |  |  |
| 4.6 | Supply and install standard metal window frame size 1200x900mm complete with handle and stays | each | 15 |  |  |
| 4.7 | Supply and install standard metal window frame size 2400x900mm complete with handle and stays | each | 8 |  |  |
| 4.8 | Supply and install standard metal window frame size 900x600mm complete with handle and stays | each | 8 |  |  |
| 4.9 | Supply and install standard metal window frame size 1800x900mm complete with handle and stays | each | 8 |  |  |
| 4.10 | Supply and apply gypsum plaster in one coat skimming finish with a steel trowel | m² | 100 |  |  |
| 4.11 | Supply and install ceramic floor tiles (Grade AAA). Including grouting and sealing. | m² | 100 |  |  |
| 4.12 | Supply and install porcelain floor tiles. (Grade AAA) including grouting and grout sealing | m² | 100 |  |  |
| 4.13 | Supply and install ceramic wall tiles(Grade AAA) including grouting and sealing | m² | 300 |  |  |
| 4.14 | Cast and install 40mm floor screed in cement/ sand mix (1:3) | m² | 150 |  |  |
| 5 | CARPENTRY SERVICES (see Section C.2.8) |  |  |  |  |
| 5.1 | Supply and install 0.5mm IBR factory painted roof sheeting including nailing and insulation | m² | 100 |  |  |
| 5.2 | Supply and install clay/cement tiles including nailing | m² | 80 |  |  |
| 5.3 | Supply and install iron roof ridge | m | 100 |  |  |
| 5.4 | Supply and install roof ridge for clay/cement tiles | m | 25 |  |  |
| 5.5 | Supply and install metal gutter | m | 100 |  |  |
| 5.6 | Supply and install PVC ceiling including edge strips | m² | 150 |  |  |
| 5.7 | Supply and install 8mm particle board ceiling | m² | 100 |  |  |
| 5.8 | Supply and install sawn 50 x 50mm softwood blandering including supports | m | 300 |  |  |
| 5.9 | Supply and install wrought softwood 225x25 mm fascias board | m | 200 |  |  |
| 5.10 | Supply and install 100mm half round PVC gutter | m | 150 |  |  |
| 5.11 | Supply and install 150mm half round PVC gutter | m | 150 |  |  |
| 5.12 | Supply and install 100mm down pipes including connection to gutter ,end outlets and wall supports | m | 60 |  |  |
| 5.13 | Supply and install standard aluminum window complete with locking, flyscreen’s and 6mm glazing. | m² | 60 |  |  |
| 5.14 | Supply and install 45mm solid core flush doors | each | 30 |  |  |
| 5.15 | Supply and install 45mm hollow core flush doors | each | 15 |  |  |
| 5.16 | Supply and install 45mm mukwa/rosewood doors | each | 30 |  |  |
| 5.17 | Supply and install 3 lever mortice lock | each | 150 |  |  |
| 5.18 | Install government supplied dead bolt locks | each | 15 |  |  |
| 5.19 | Supply and install 150 X50mm rafters including painting with preservative | m | 200 |  |  |
| 5.20 | Supply and install 100 X 38mm rafters including painting with preservative and nailing | m | 200 |  |  |
| 5.21 | Supply and install 75 X50mm purlins including painting with preservative and nailing | m | 300 |  |  |
| 5.22 | Supply and Install shelving in cabinets using 18mm block boards | m² | 80 |  |  |
| 5.23 | Supply and Install double rod wooden curtain rails including supports size 2500m | each | 50 |  |  |
| 5.24 | Supply and Install double rod metal curtain rails including supports, | each | 50 |  |  |
| 5.25 | Supply and install suspended ceiling as 10mm rhinoboard or other equal approved plasterboard with skimmed plaster fixed already existing 50x50mm branders including joint tape and cornice | m² | 150 |  |  |
| 5.26 | Replace wooden framed screen door 2000 x900mm | each | 20 |  |  |
| 5.27 | Replace aluminum framed screen door 2000 x900mm | each | 20 |  |  |
| 5.28 | Replace fly screen including frame to windows 900x600mm | each | 60 |  |  |
| 5.29 | Supply and install door stopper | each | 200 |  |  |
| 5.30 | Supply and install parquet wood floor | m² | 200 |  |  |
| 5.31 | Supply and install 400x75x20mm teak wood floor | m² | 150 |  |  |
| 5.32 | Supply and install 400x75x20mm rosewood wood floor | m² | 100 |  |  |
| 5.33 | Supply and install 100mm x 20mm wood base board | m | 400 |  |  |
| 5.34 | Supply and install 75mm softwood cornice | m | 400 |  |  |
| 5.35 | Supply and install 40mm softwood cover strips | m | 250 |  |  |
| 5.36 | Supply install 100mm butt hinges complete with screws | each | 80 |  |  |
| 5.37 | Supply and install aluminum weather strips 900mm | each | 30 |  |  |
| 5.38 | Supply and install 6mm clear glass including putty | m² | 40 |  |  |
| 5.39 | Supply and install 3mm clear glass including putty | m² | 40 |  |  |
| 5.40 | Supply and install 6mm obscure glass including putty | m² | 15 |  |  |
| 5.41 | Supply and install 3mm obscure glass including putty | m² | 15 |  |  |
| 5.42 | Check and repair sticky hinges doors, drawers and sliding doors. Per house | lot | 14 |  |  |
| 5.43 | Clean chimneys and fireplaces per house | each | 10 |  |  |
| 5.44 | Replace 30mm granite counter tops 600mm | m | 25 |  |  |
| 5.45 | Replace cabinet hinges per house | each | 14 |  |  |
| 5.46 | Repair leaky roof using roof membrane /house | lot | 10 |  |  |
| 5.47 | Replace caulking around the bathtub and kitchen sink | m | 30 |  |  |
| 5.48 | Supply and install coat hooks | each | 20 |  |  |
| 5.49 | Supply and install soap holder | each | 20 |  |  |
| 5.50 | Supply and install toilet roll holder | each | 20 |  |  |
| 5.51 | Supply and install 25mm shower curtain rod complete with end brackets. | m | 25 |  |  |
| 5.52 | Supply and install insulation in the ceiling. | m² | 150 |  |  |
| 5.53 | Supply and install 1.6mm vinyl composition tile floor 300 x300mm including supply of adhesive. | m² | 80 |  |  |
| 5.54 | Supply and replace aluminum screen materials for doors or windows | m² | 80 |  |  |
| 5.55 | Supply and replace wooden door frame complete with trims | each | 20 |  |  |
| 5.56 | Supply and install quarter round wood mouldings | m | 100 |  |  |
| 6 | PLUMBING SERVICES (see Section C.2.5) |  |  |  |  |
| 6.1 | Check and test all plumbing fixtures and snake out all interior drain lines | lot | 8 |  |  |
| 6.2 | Replace 20mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.3 | Replace 12mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.4 | Replace kitchen double bowl sink | each | 8 |  |  |
| 6.5 | Replace swing kitchen faucet Cobra or similar quality | each | 10 |  |  |
| 6.6 | Replace P trap for kitchen sink | each | 20 |  |  |
| 6.7 | Replace wash hand basin of high quality | each | 15 |  |  |
| 6.8 | Supply and replace 12mm copper/flexi connector | each | 30 |  |  |
| 6.9 | Supply and replace 20mm copper/flexi connector | each | 30 |  |  |
| 6.10 | Supply and install 20mm CPVC gate valves | each | 150 |  |  |
| 6.11 | Supply and install 12mm CPVC gate valves | each | 150 |  |  |
| 6.12 | Supply and install connection from GI to CPVC 20mm | each | 40 |  |  |
| 6.13 | Supply and install connection from GI to CPVC 12mm | each | 40 |  |  |
| 6.14 | Supply and install 40mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.15 | Supply and install 50mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.16 | Supply and install 110mm PVC pipes complete with fittings | m | 400 |  |  |
| 6.17 | Supply and install telephone bath mixer 20mm | each | 20 |  |  |
| 6.18 | Supply and install 500x500 manhole cover | each | 15 |  |  |
| 6.19 | Supply and install shower valve and mixing assembly 20mm | each | 10 |  |  |
| 6.20 | Supply and install shower head | each | 20 |  |  |
| 6.21 | Supply and install toilet pan complete with cistern | each | 25 |  |  |
| 6.22 | Supply and install seat cover | each | 25 |  |  |
| 6.23 | Supply and install WHB mixer 12mm | each | 25 |  |  |
| 6.24 | Supply and install shower cubicle 1200x900 as supplied by Make a Home with tempered glass panels or similar | each | 10 |  |  |
| 6.25 | Supply and install bathtub 1700x600x450mm deep | each | 10 |  |  |
| 6.26 | Supply and install 6mm mirror complete with dome screws and caps | each | 20 |  |  |
| 6.27 | Chisel for piping in wall 50mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.28 | Chisel for piping in slab 70mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.29 | Chisel for piping through 100mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.30 | Chisel for piping through 150mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.31 | Chisel for piping through 200mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.32 | Supply and install 100 ltrs water heater | each | 20 |  |  |
| 6.33 | Service water heater by removing accumulation of scale, clean element with vinegar and re-install | lot | 10 |  |  |
| 6.34 | Supply and install 2KW heating element complete with thermostat. | each | 20 |  |  |
| 6.35 | Install valve labels | lot | 10 |  |  |
| 6.36 | Supply and install shut off valves 20mm | lot | 10 |  |  |
| 6.37 | Remove scale from mixers | lot | 10 |  |  |
| 7 | ELECTRICAL SERVICES (see Section C.2.6) |  |  |  |  |
| 7.1 | Replace existing light switches | each | 150 |  |  |
| 7.2 | Replace existing electrical outlets | each | 250 |  |  |
| 7.3 | Replace MCBs single pole 20Amps | each | 100 |  |  |
| 7.4 | Replace MCBs single pole 10Amps | each | 100 |  |  |
| 7.5 | Replace MCBs single pole 30Amps | each | 100 |  |  |
| 7.6 | Replace MCBs single pole 40Amps | each | 100 |  |  |
| 7.7 | Replace MCBs single pole 60Amps | each | 60 |  |  |
| 7.8 | Replace MCBs single pole 80Amps | each | 60 |  |  |
| 7.9 | Replace MCBs tripple pole 20Amps | each | 20 |  |  |
| 7.10 | Replace MCBs tripple pole 60Amps | each | 20 |  |  |
| 7.11 | Replace MCBs tripple pole 80Amps | each | 20 |  |  |
| 7.12 | Supply and install 1.5mm 2 cable red | m | 4000 |  |  |
| 7.13 | Supply and install 2.5mm 2 cable red | m | 4000 |  |  |
| 7.14 | Supply and install 4mm 2 cable red | m | 2500 |  |  |
| 7.15 | Supply and install 6mm 2 cable red | m | 1000 |  |  |
| 7.16 | supply and install 4 ft single fluorescent light fitting | each | 200 |  |  |
| 7.17 | supply and install 2 ft single fluorescent light fitting | each | 20 |  |  |
| 7.18 | supply and install 4 ft double fluorescent light fitting | each | 200 |  |  |
| 7.19 | supply and install 2 ft double fluorescent light fitting | each | 20 |  |  |
| 7.20 | supply and install recessed vapor barrier light fixture | each | 80 |  |  |
| 7.21 | Supply and install 6" spherical light fitting | each | 80 |  |  |
| 7.22 | Supply and install 8" spherical light fitting | each | 80 |  |  |
| 7.23 | Install government supplied chandelier | each | 20 |  |  |
| 7.24 | Install government supplied ceiling fan | each | 30 |  |  |
| 7.25 | Install government supplied GFCI socket outlets | each | 30 |  |  |
| 7.26 | Install government supplied door bell | each | 15 |  |  |
| 7.27 | Supply and install 20mm PVC electrical conduits | m | 1000 |  |  |
| 7.28 | Supply and install 25mm PVC electrical conduits | m | 1000 |  |  |
| 7.29 | Supply and install metal boxes 3"x3" | each | 300 |  |  |
| 7.30 | Supply and install metal boxes 6"x3" | each | 300 |  |  |
| 7.31 | Supply and install junction boxes complete with covers | each | 300 |  |  |
| 7.32 | Replace geyser switches | each | 30 |  |  |
| 7.33 | Supply and install light bulbs | each | 300 |  |  |
| 7.34 | supply and install lightening arrestors | each | 60 |  |  |
| 7.35 | Label distribution panel | lot | 10 |  |  |
| 7.36 | Install dead front panel | lot | 10 |  |  |
| 8 | PAINTING SERVICES (See Section C.2.1.4) |  |  |  |  |
| 8.1 | Clean old paint, repair plaster, prime and smooth surface, apply (1) coat of interior undercoat paint to walls and ceiling | m² | 2500 |  |  |
| 8.2 | Colored painting walls, two coats, (semi-gloss) paint, no surface preparation | m² | 4000 |  |  |
| 8.3 | Painting ceilings, two coats, (PVA) paint, no surface preparation | m² | 3000 |  |  |
| 8.4 | Paint, exterior oil 2 coat | m² | 800 |  |  |
| 8.5 | Paint, exterior latex, 2coat | m² | 2000 |  |  |
| 8.6 | Paint, exterior enamel,2coats | m² | 1000 |  |  |
| 8.7 | Paint, interior latex, 2 coat | m² | 2000 |  |  |
| 8.8 | Painting trim/baseboards, one coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.9 | Varnishing of woodwork, following surface preparation | m² | 1000 |  |  |
| 8.10 | Textured Surfaces preparatory work | m² | 1000 |  |  |
| 8.11 | Painting of textured surfaces, one coat, (latex semi-gloss, spray application incl. Floor coverings, etc.) | m² | 1000 |  |  |
| 8.12 | Prepare surface and apply ceiling texture (spray application incl. Floor coverings, etc.) | m² | 600 |  |  |
| 8.13 | Painting wood surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 600 |  |  |
| 8.14 | Painting metal surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 200 |  |  |
| 8.15 | Painting wood surfaces( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.16 | Painting metal surfaces ( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 9 | HVAC SERVICES (see Section C.2.7) |  |  |  |  |
| 9.1 | Install indoor Evaporator units. | each | 40 |  |  |
| 9.2 | Install outside condensing units | each | 40 |  |  |
| 9.3 | Install refrigeration lines/pipes between the inside and outside units. The refrigeration lines/pipes between the inside and outside units must be installed following a route and in a manner acceptable to the Contracting Officer Representative. Insulate all pipes with Armaflex | each | 40 |  |  |
| 9.4 | Install all pipes in Trunkings and provide for Air-conditioning drain. | each | 40 |  |  |
| 9.5 | Install thermostat holder. The location where the thermostat will be installed will be coordinated with the contracting Officer Representative. | each | 40 |  |  |
| 9.6 | Provide for an Isolation switch for the indoor and outdoor unit | each | 40 |  |  |
| 9.7 | Install electrical power and signal cable between indoor and outdoor unit. | each | 40 |  |  |
| 9.8 | The new AC units must be tested for proper operation. The contractor must demonstrate to the Contracting Officer Representatives that the system functions properly before the project will be accepted. | each | 40 |  |  |
| 9.9 | Carry out full service of the existing ACs as described in C.2.4 (c ) | each | 40 |  |  |
|  | Total of all line-item prices: |  |  |  |  |
|  | First Option year total |  |  |  |  |

*m² – square meter

### The estimated amounts are based on total estimated Government requirements.  This means that if more than one award is made, the estimated amount of work awarded under task order(s) to any single contractor will be less than the amount shown.

### B.3.5	SECOND OPTION YEAR PRICES

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
| 1 | DEMOLITION SERVICES |  |  |  |  |
| 1.1 | Demolish existing concrete slab, remove debris from site and cart away to contractor's dump site(average thickness 150mm) | m³ | 7 |  |  |
| 1.2 | Demolish existing masonry wall including plaster, remove debris from site and cart away to contractor's dump site | m² | 70 |  |  |
| 1.3 | Carefully remove roof covering and all damaged purlin and roof structure, remove debris from site and cart away to contractor's dump site | m² | 60 |  |  |
| 1.4 | Remove existing gutters ,remove debris from and cart away to contractors dump site | m | 150 |  |  |
| 1.5 | Remove existing fascial board, remove debris from site and cart away to contractor’s dump site | m | 150 |  |  |
| 1.6 | Remove all existing wall tiles, remove debris from site and cart away to contractor's dump site | m | 60 |  |  |
| 1.7 | Remove all existing floor covering, remove debris from site and cart away to contractor's dump site | m² | 200 |  |  |
| 1.8 | Remove existing door frames including lintol , remove debris and hand over frame to client or cart away to contractor’s dump site | each | 15 |  |  |
| 1.9 | Remove existing window frames including lintol , remove debris and hand over frame to client or cart away to contractor's dump site | lot | 7 |  |  |
| 1.10 | Remove existing bathtub ,wash hand basin and toilet pan, clean drain and hand over to the COR | lot | 8 |  |  |
| 1.11 | Remove all plumbing piping , remove debris and cart away to contractor’s dump site | lot | 8 |  |  |
| 1.12 | Removing existing particle board/gypsum board ceiling including blundering, remove debris and cart away. | m² | 150 |  |  |
| 1.13 | Remove existing wall cabinets and hand over to the COR | lot | 7 |  |  |
| 1.14 | Remove existing curtain rails and supports. Hand over to the COR | m | 100 |  |  |
| 1.15 | Carefully remove all distribution panel boards including all cabling and take away from site | lot | 7 |  |  |
| 1.16 | Carefully remove all electrical light fittings including switches and cabling and take away from site | lot | 7 |  |  |
| 1.17 | Carefully remove all sockets including all cabling and take away from site | lot | 7 |  |  |
| 2 | CONCRETE SERVICES |  |  |  |  |
| 2.1 | Supply and cast plain concrete grade 20/20 mm aggregate. | m³ | 10 |  |  |
| 2.2 | Supply and cast vibrated reinforced concrete grade 25/20 mm aggregate. | m³ | 8 |  |  |
| 2.3 | Supply and lay deformed steel bars reinforcement (varies sizes) | kg | 100 |  |  |
| 2.4 | Supply and lay steel mesh fabric reinforcement conforce 257 allowing 200mm lap at joints | m² | 20 |  |  |
| 2.5 | Supply and lay steel mesh fabric reinforcement conforce 86 allowing 200mm lap at joints | m² | 25 |  |  |
| 2.6 | Formworks for sides of columns, steps edges of the beds | m² | 120 |  |  |
| 2.7 | Repair crack concrete screed chip off 25mm wide V joint seal with cement grout | m | 60 |  |  |
| 3 | SITE SERVICES |  |  |  |  |
| 3.1 | Clear site of works of shrubs, bushes and trees | m² | 50 |  |  |
| 3.2 | Excavate around foundation not exceeding 1m deep | m³ | 10 |  |  |
| 3.3 | Excavate to remove top soil and load and cart away to contractors tipping site average depth 150mm | m² | 70 |  |  |
| 3.4 | load and cart away surplus spoil to contractor’s dump site | m³ | 60 |  |  |
| 3.5 | Backfill and compact in layers not exceeding 150mm | m³ | 90 |  |  |
| 3.6 | Supply and install 500 gauge polythene laid under surface beds | m² | 90 |  |  |
| 3.7 | Apply approved ant termite treatment | m² | 90 |  |  |
| 4 | MASONRY SERVICES (See section C.2.11) |  |  |  |  |
| 4.1 | Erect hollow block walling (3.5N/m2 crushing strength) in cement mortar allow for brick force reinforcement every 3 courses |  |  |  |  |
| 4.1.1 | 200mm walls | m² | 60 |  |  |
| 4.1.2 | 150mm walls | m² | 80 |  |  |
| 4.1.3 | 100mm walls | m² | 70 |  |  |
| 4.2 | Erect Solid block/brick walling (5.0N/m2 crushing strength) in cement mortar and allowing for brick force reinforcement every 3 courses |  |  |  |  |
| 4.2.1 | 200mm walls | m² | 40 |  |  |
| 4.2.2 | 150mm walls | m² | 50 |  |  |
| 4.2.3 | 100mm walls | m² | 30 |  |  |
| 4.3 | Cement /sand plaster |  |  |  |  |
| 4.3.1 | Cement/sand (1:4) external rendering 20mm thick in wood float finish | m² | 100 |  |  |
| 4.3.2 | Cement/sand (1:3) internal rendering 20mm thick in steel trowelled smooth finish | m² | 100 |  |  |
| 4.3.3 | Plaster to reveal and returns | m | 100 |  |  |
| 4.4 | Beam filling between wall and roof | m | 100 |  |  |
| 4.5 | Supply and install 14g standard pressed steel door frame, double rebated including hinges, masonry, jamps and striking plate. | each | 15 |  |  |
| 4.6 | Supply and install standard metal window frame size 1200x900mm complete with handle and stays | each | 15 |  |  |
| 4.7 | Supply and install standard metal window frame size 2400x900mm complete with handle and stays | each | 8 |  |  |
| 4.8 | Supply and install standard metal window frame size 900x600mm complete with handle and stays | each | 8 |  |  |
| 4.9 | Supply and install standard metal window frame size 1800x900mm complete with handle and stays | each | 8 |  |  |
| 4.10 | Supply and apply gypsum plaster in one coat skimming finish with a steel trowel | m² | 100 |  |  |
| 4.11 | Supply and install ceramic floor tiles (Grade AAA). Including grouting and sealing. | m² | 100 |  |  |
| 4.12 | Supply and install porcelain floor tiles. (Grade AAA) including grouting and grout sealing | m² | 100 |  |  |
| 4.13 | Supply and install ceramic wall tiles(Grade AAA) including grouting and sealing | m² | 300 |  |  |
| 4.14 | Cast and install 40mm floor screed in cement/ sand mix (1:3) | m² | 150 |  |  |
| 5 | CARPENTRY SERVICES (see Section C.2.8) |  |  |  |  |
| 5.1 | Supply and install 0.5mm IBR factory painted roof sheeting including nailing and insulation | m² | 100 |  |  |
| 5.2 | Supply and install clay/cement tiles including nailing | m² | 80 |  |  |
| 5.3 | Supply and install iron roof ridge | m | 100 |  |  |
| 5.4 | Supply and install roof ridge for clay/cement tiles | m | 25 |  |  |
| 5.5 | Supply and install metal gutter | m | 100 |  |  |
| 5.6 | Supply and install PVC ceiling including edge strips | m² | 150 |  |  |
| 5.7 | Supply and install 8mm particle board ceiling | m² | 100 |  |  |
| 5.8 | Supply and install sawn 50 x 50mm softwood blandering including supports | m | 300 |  |  |
| 5.9 | Supply and install wrought softwood 225x25 mm fascias board | m | 200 |  |  |
| 5.10 | Supply and install 100mm half round PVC gutter | m | 150 |  |  |
| 5.11 | Supply and install 150mm half round PVC gutter | m | 150 |  |  |
| 5.12 | Supply and install 100mm down pipes including connection to gutter ,end outlets and wall supports | m | 60 |  |  |
| 5.13 | Supply and install standard aluminum window complete with locking, flyscreen’s and 6mm glazing. | m² | 60 |  |  |
| 5.14 | Supply and install 45mm solid core flush doors | each | 30 |  |  |
| 5.15 | Supply and install 45mm hollow core flush doors | each | 15 |  |  |
| 5.16 | Supply and install 45mm mukwa/rosewood doors | each | 30 |  |  |
| 5.17 | Supply and install 3 lever mortice lock | each | 150 |  |  |
| 5.18 | Install government supplied dead bolt locks | each | 15 |  |  |
| 5.19 | Supply and install 150 X50mm rafters including painting with preservative | m | 200 |  |  |
| 5.20 | Supply and install 100 X 38mm rafters including painting with preservative and nailing | m | 200 |  |  |
| 5.21 | Supply and install 75 X50mm purlins including painting with preservative and nailing | m | 300 |  |  |
| 5.22 | Supply and Install shelving in cabinets using 18mm block boards | m² | 80 |  |  |
| 5.23 | Supply and Install double rod wooden curtain rails including supports size 2500m | each | 50 |  |  |
| 5.24 | Supply and Install double rod metal curtain rails including supports, | each | 50 |  |  |
| 5.25 | Supply and install suspended ceiling as 10mm rhinoboard or other equal approved plasterboard with skimmed plaster fixed already existing 50x50mm branders including joint tape and cornice | m² | 150 |  |  |
| 5.26 | Replace wooden framed screen door 2000 x900mm | each | 20 |  |  |
| 5.27 | Replace aluminum framed screen door 2000 x900mm | each | 20 |  |  |
| 5.28 | Replace fly screen including frame to windows 900x600mm | each | 60 |  |  |
| 5.29 | Supply and install door stopper | each | 200 |  |  |
| 5.30 | Supply and install parquet wood floor | m² | 200 |  |  |
| 5.31 | Supply and install 400x75x20mm teak wood floor | m² | 150 |  |  |
| 5.32 | Supply and install 400x75x20mm rosewood wood floor | m² | 100 |  |  |
| 5.33 | Supply and install 100mm x 20mm wood base board | m | 400 |  |  |
| 5.34 | Supply and install 75mm softwood cornice | m | 400 |  |  |
| 5.35 | Supply and install 40mm softwood cover strips | m | 250 |  |  |
| 5.36 | Supply install 100mm butt hinges complete with screws | each | 80 |  |  |
| 5.37 | Supply and install aluminum weather strips 900mm | each | 30 |  |  |
| 5.38 | Supply and install 6mm clear glass including putty | m² | 40 |  |  |
| 5.39 | Supply and install 3mm clear glass including putty | m² | 40 |  |  |
| 5.40 | Supply and install 6mm obscure glass including putty | m² | 15 |  |  |
| 5.41 | Supply and install 3mm obscure glass including putty | m² | 15 |  |  |
| 5.42 | Check and repair sticky hinges doors, drawers and sliding doors. Per house | lot | 14 |  |  |
| 5.43 | Clean chimneys and fireplaces per house | each | 10 |  |  |
| 5.44 | Replace 30mm granite counter tops 600mm | m | 25 |  |  |
| 5.45 | Replace cabinet hinges per house | each | 14 |  |  |
| 5.46 | Repair leaky roof using roof membrane /house | lot | 10 |  |  |
| 5.47 | Replace caulking around the bathtub and kitchen sink | m | 30 |  |  |
| 5.48 | Supply and install coat hooks | each | 20 |  |  |
| 5.49 | Supply and install soap holder | each | 20 |  |  |
| 5.50 | Supply and install toilet roll holder | each | 20 |  |  |
| 5.51 | Supply and install 25mm shower curtain rod complete with end brackets. | m | 25 |  |  |
| 5.52 | Supply and install insulation in the ceiling. | m² | 150 |  |  |
| 5.53 | Supply and install 1.6mm vinyl composition tile floor 300 x300mm including supply of adhesive. | m² | 80 |  |  |
| 5.54 | Supply and replace aluminum screen materials for doors or windows | m² | 80 |  |  |
| 5.55 | Supply and replace wooden door frame complete with trims | each | 20 |  |  |
| 5.56 | Supply and install quarter round wood mouldings | m | 100 |  |  |
| 6 | PLUMBING SERVICES (see Section C.2.5) |  |  |  |  |
| 6.1 | Check and test all plumbing fixtures and snake out all interior drain lines | lot | 8 |  |  |
| 6.2 | Replace 20mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.3 | Replace 12mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.4 | Replace kitchen double bowl sink | each | 8 |  |  |
| 6.5 | Replace swing kitchen faucet Cobra or similar quality | each | 10 |  |  |
| 6.6 | Replace P trap for kitchen sink | each | 20 |  |  |
| 6.7 | Replace wash hand basin of high quality | each | 15 |  |  |
| 6.8 | Supply and replace 12mm copper/flexi connector | each | 30 |  |  |
| 6.9 | Supply and replace 20mm copper/flexi connector | each | 30 |  |  |
| 6.10 | Supply and install 20mm CPVC gate valves | each | 150 |  |  |
| 6.11 | Supply and install 12mm CPVC gate valves | each | 150 |  |  |
| 6.12 | Supply and install connection from GI to CPVC 20mm | each | 40 |  |  |
| 6.13 | Supply and install connection from GI to CPVC 12mm | each | 40 |  |  |
| 6.14 | Supply and install 40mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.15 | Supply and install 50mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.16 | Supply and install 110mm PVC pipes complete with fittings | m | 400 |  |  |
| 6.17 | Supply and install telephone bath mixer 20mm | each | 20 |  |  |
| 6.18 | Supply and install 500x500 manhole cover | each | 15 |  |  |
| 6.19 | Supply and install shower valve and mixing assembly 20mm | each | 10 |  |  |
| 6.20 | Supply and install shower head | each | 20 |  |  |
| 6.21 | Supply and install toilet pan complete with cistern | each | 25 |  |  |
| 6.22 | Supply and install seat cover | each | 25 |  |  |
| 6.23 | Supply and install WHB mixer 12mm | each | 25 |  |  |
| 6.24 | Supply and install shower cubicle 1200x900 as supplied by Make a Home with tempered glass panels or similar | each | 10 |  |  |
| 6.25 | Supply and install bathtub 1700x600x450mm deep | each | 10 |  |  |
| 6.26 | Supply and install 6mm mirror complete with dome screws and caps | each | 20 |  |  |
| 6.27 | Chisel for piping in wall 50mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.28 | Chisel for piping in slab 70mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.29 | Chisel for piping through 100mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.30 | Chisel for piping through 150mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.31 | Chisel for piping through 200mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.32 | Supply and install 100 ltrs water heater | each | 20 |  |  |
| 6.33 | Service water heater by removing accumulation of scale, clean element with vinegar and re-install | lot | 10 |  |  |
| 6.34 | Supply and install 2KW heating element complete with thermostat. | each | 20 |  |  |
| 6.35 | Install valve labels | lot | 10 |  |  |
| 6.36 | Supply and install shut off valves 20mm | lot | 10 |  |  |
| 6.37 | Remove scale from mixers | lot | 10 |  |  |
| 7 | ELECTRICAL SERVICES (see Section C.2.6) |  |  |  |  |
| 7.1 | Replace existing light switches | each | 150 |  |  |
| 7.2 | Replace existing electrical outlets | each | 250 |  |  |
| 7.3 | Replace MCBs single pole 20Amps | each | 100 |  |  |
| 7.4 | Replace MCBs single pole 10Amps | each | 100 |  |  |
| 7.5 | Replace MCBs single pole 30Amps | each | 100 |  |  |
| 7.6 | Replace MCBs single pole 40Amps | each | 100 |  |  |
| 7.7 | Replace MCBs single pole 60Amps | each | 60 |  |  |
| 7.8 | Replace MCBs single pole 80Amps | each | 60 |  |  |
| 7.9 | Replace MCBs tripple pole 20Amps | each | 20 |  |  |
| 7.10 | Replace MCBs tripple pole 60Amps | each | 20 |  |  |
| 7.11 | Replace MCBs tripple pole 80Amps | each | 20 |  |  |
| 7.12 | Supply and install 1.5mm 2 cable red | m | 4000 |  |  |
| 7.13 | Supply and install 2.5mm 2 cable red | m | 4000 |  |  |
| 7.14 | Supply and install 4mm 2 cable red | m | 2500 |  |  |
| 7.15 | Supply and install 6mm 2 cable red | m | 1000 |  |  |
| 7.16 | supply and install 4 ft single fluorescent light fitting | each | 200 |  |  |
| 7.17 | supply and install 2 ft single fluorescent light fitting | each | 20 |  |  |
| 7.18 | supply and install 4 ft double fluorescent light fitting | each | 200 |  |  |
| 7.19 | supply and install 2 ft double fluorescent light fitting | each | 20 |  |  |
| 7.20 | supply and install recessed vapor barrier light fixture | each | 80 |  |  |
| 7.21 | Supply and install 6" spherical light fitting | each | 80 |  |  |
| 7.22 | Supply and install 8" spherical light fitting | each | 80 |  |  |
| 7.23 | Install government supplied chandelier | each | 20 |  |  |
| 7.24 | Install government supplied ceiling fan | each | 30 |  |  |
| 7.25 | Install government supplied GFCI socket outlets | each | 30 |  |  |
| 7.26 | Install government supplied door bell | each | 15 |  |  |
| 7.27 | Supply and install 20mm PVC electrical conduits | m | 1000 |  |  |
| 7.28 | Supply and install 25mm PVC electrical conduits | m | 1000 |  |  |
| 7.29 | Supply and install metal boxes 3"x3" | each | 300 |  |  |
| 7.30 | Supply and install metal boxes 6"x3" | each | 300 |  |  |
| 7.31 | Supply and install junction boxes complete with covers | each | 300 |  |  |
| 7.32 | Replace geyser switches | each | 30 |  |  |
| 7.33 | Supply and install light bulbs | each | 300 |  |  |
| 7.34 | supply and install lightening arrestors | each | 60 |  |  |
| 7.35 | Label distribution panel | lot | 10 |  |  |
| 7.36 | Install dead front panel | lot | 10 |  |  |
| 8 | PAINTING SERVICES (See Section C.2.1.4) |  |  |  |  |
| 8.1 | Clean old paint, repair plaster, prime and smooth surface, apply (1) coat of interior undercoat paint to walls and ceiling | m² | 2500 |  |  |
| 8.2 | Colored painting walls, two coats, (semi-gloss) paint, no surface preparation | m² | 4000 |  |  |
| 8.3 | Painting ceilings, two coats, (PVA) paint, no surface preparation | m² | 3000 |  |  |
| 8.4 | Paint, exterior oil 2 coat | m² | 800 |  |  |
| 8.5 | Paint, exterior latex, 2coat | m² | 2000 |  |  |
| 8.6 | Paint, exterior enamel,2coats | m² | 1000 |  |  |
| 8.7 | Paint, interior latex, 2 coat | m² | 2000 |  |  |
| 8.8 | Painting trim/baseboards, one coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.9 | Varnishing of woodwork, following surface preparation | m² | 1000 |  |  |
| 8.10 | Textured Surfaces preparatory work | m² | 1000 |  |  |
| 8.11 | Painting of textured surfaces, one coat, (latex semi-gloss, spray application incl. Floor coverings, etc.) | m² | 1000 |  |  |
| 8.12 | Prepare surface and apply ceiling texture (spray application incl. Floor coverings, etc.) | m² | 600 |  |  |
| 8.13 | Painting wood surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 600 |  |  |
| 8.14 | Painting metal surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 200 |  |  |
| 8.15 | Painting wood surfaces( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.16 | Painting metal surfaces ( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 9 | HVAC SERVICES (see Section C.2.7) |  |  |  |  |
| 9.1 | Install indoor Evaporator units. | each | 40 |  |  |
| 9.2 | Install outside condensing units | each | 40 |  |  |
| 9.3 | Install refrigeration lines/pipes between the inside and outside units. The refrigeration lines/pipes between the inside and outside units must be installed following a route and in a manner acceptable to the Contracting Officer Representative. Insulate all pipes with Armaflex | each | 40 |  |  |
| 9.4 | Install all pipes in Trunkings and provide for Air-conditioning drain. | each | 40 |  |  |
| 9.5 | Install thermostat holder. The location where the thermostat will be installed will be coordinated with the contracting Officer Representative. | each | 40 |  |  |
| 9.6 | Provide for an Isolation switch for the indoor and outdoor unit | each | 40 |  |  |
| 9.7 | Install electrical power and signal cable between indoor and outdoor unit. | each | 40 |  |  |
| 9.8 | The new AC units must be tested for proper operation. The contractor must demonstrate to the Contracting Officer Representatives that the system functions properly before the project will be accepted. | each | 40 |  |  |
| 9.9 | Carry out full service of the existing ACs as described in C.2.4 (c ) | each | 40 |  |  |
|  | Total of all line-item prices: |  |  |  |  |
|  | Second option year total |  |  |  |  |

*m² – square meter

The estimated amounts are based on total estimated Government requirements.  This means that if more than one award is made, the estimated amount of work awarded under task order(s) to any single contractor will be less than the amount shown.

B.3.6	THIRD OPTION YEAR PRICES

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
| 1 | DEMOLITION SERVICES |  |  |  |  |
| 1.1 | Demolish existing concrete slab, remove debris from site and cart away to contractor's dump site(average thickness 150mm) | m³ | 7 |  |  |
| 1.2 | Demolish existing masonry wall including plaster, remove debris from site and cart away to contractor's dump site | m² | 70 |  |  |
| 1.3 | Carefully remove roof covering and all damaged purlin and roof structure, remove debris from site and cart away to contractor's dump site | m² | 60 |  |  |
| 1.4 | Remove existing gutters ,remove debris from and cart away to contractors dump site | m | 150 |  |  |
| 1.5 | Remove existing fascial board, remove debris from site and cart away to contractor’s dump site | m | 150 |  |  |
| 1.6 | Remove all existing wall tiles, remove debris from site and cart away to contractor's dump site | m | 60 |  |  |
| 1.7 | Remove all existing floor covering, remove debris from site and cart away to contractor's dump site | m² | 200 |  |  |
| 1.8 | Remove existing door frames including lintol , remove debris and hand over frame to client or cart away to contractor’s dump site | each | 15 |  |  |
| 1.9 | Remove existing window frames including lintol , remove debris and hand over frame to client or cart away to contractor's dump site | lot | 7 |  |  |
| 1.10 | Remove existing bathtub ,wash hand basin and toilet pan, clean drain and hand over to the COR | lot | 8 |  |  |
| 1.11 | Remove all plumbing piping , remove debris and cart away to contractor’s dump site | lot | 8 |  |  |
| 1.12 | Removing existing particle board/gypsum board ceiling including blundering, remove debris and cart away. | m² | 150 |  |  |
| 1.13 | Remove existing wall cabinets and hand over to the COR | lot | 7 |  |  |
| 1.14 | Remove existing curtain rails and supports. Hand over to the COR | m | 100 |  |  |
| 1.15 | Carefully remove all distribution panel boards including all cabling and take away from site | lot | 7 |  |  |
| 1.16 | Carefully remove all electrical light fittings including switches and cabling and take away from site | lot | 7 |  |  |
| 1.17 | Carefully remove all sockets including all cabling and take away from site | lot | 7 |  |  |
| 2 | CONCRETE SERVICES |  |  |  |  |
| 2.1 | Supply and cast plain concrete grade 20/20 mm aggregate. | m³ | 10 |  |  |
| 2.2 | Supply and cast vibrated reinforced concrete grade 25/20 mm aggregate. | m³ | 8 |  |  |
| 2.3 | Supply and lay deformed steel bars reinforcement (varies sizes) | kg | 100 |  |  |
| 2.4 | Supply and lay steel mesh fabric reinforcement conforce 257 allowing 200mm lap at joints | m² | 20 |  |  |
| 2.5 | Supply and lay steel mesh fabric reinforcement conforce 86 allowing 200mm lap at joints | m² | 25 |  |  |
| 2.6 | Formworks for sides of columns, steps edges of the beds | m² | 120 |  |  |
| 2.7 | Repair crack concrete screed chip off 25mm wide V joint seal with cement grout | m | 60 |  |  |
| 3 | SITE SERVICES |  |  |  |  |
| 3.1 | Clear site of works of shrubs, bushes and trees | m² | 50 |  |  |
| 3.2 | Excavate around foundation not exceeding 1m deep | m³ | 10 |  |  |
| 3.3 | Excavate to remove top soil and load and cart away to contractors tipping site average depth 150mm | m² | 70 |  |  |
| 3.4 | load and cart away surplus spoil to contractor’s dump site | m³ | 60 |  |  |
| 3.5 | Backfill and compact in layers not exceeding 150mm | m³ | 90 |  |  |
| 3.6 | Supply and install 500 gauge polythene laid under surface beds | m² | 90 |  |  |
| 3.7 | Apply approved ant termite treatment | m² | 90 |  |  |
| 4 | MASONRY SERVICES (See section C.2.11) |  |  |  |  |
| 4.1 | Erect hollow block walling (3.5N/m2 crushing strength) in cement mortar allow for brick force reinforcement every 3 courses |  |  |  |  |
| 4.1.1 | 200mm walls | m² | 60 |  |  |
| 4.1.2 | 150mm walls | m² | 80 |  |  |
| 4.1.3 | 100mm walls | m² | 70 |  |  |
| 4.2 | Erect Solid block/brick walling (5.0N/m2 crushing strength) in cement mortar and allowing for brick force reinforcement every 3 courses |  |  |  |  |
| 4.2.1 | 200mm walls | m² | 40 |  |  |
| 4.2.2 | 150mm walls | m² | 50 |  |  |
| 4.2.3 | 100mm walls | m² | 30 |  |  |
| 4.3 | Cement /sand plaster |  |  |  |  |
| 4.3.1 | Cement/sand (1:4) external rendering 20mm thick in wood float finish | m² | 100 |  |  |
| 4.3.2 | Cement/sand (1:3) internal rendering 20mm thick in steel trowelled smooth finish | m² | 100 |  |  |
| 4.3.3 | Plaster to reveal and returns | m | 100 |  |  |
| 4.4 | Beam filling between wall and roof | m | 100 |  |  |
| 4.5 | Supply and install 14g standard pressed steel door frame, double rebated including hinges, masonry, jamps and striking plate. | each | 15 |  |  |
| 4.6 | Supply and install standard metal window frame size 1200x900mm complete with handle and stays | each | 15 |  |  |
| 4.7 | Supply and install standard metal window frame size 2400x900mm complete with handle and stays | each | 8 |  |  |
| 4.8 | Supply and install standard metal window frame size 900x600mm complete with handle and stays | each | 8 |  |  |
| 4.9 | Supply and install standard metal window frame size 1800x900mm complete with handle and stays | each | 8 |  |  |
| 4.10 | Supply and apply gypsum plaster in one coat skimming finish with a steel trowel | m² | 100 |  |  |
| 4.11 | Supply and install ceramic floor tiles (Grade AAA). Including grouting and sealing. | m² | 100 |  |  |
| 4.12 | Supply and install porcelain floor tiles. (Grade AAA) including grouting and grout sealing | m² | 100 |  |  |
| 4.13 | Supply and install ceramic wall tiles(Grade AAA) including grouting and sealing | m² | 300 |  |  |
| 4.14 | Cast and install 40mm floor screed in cement/ sand mix (1:3) | m² | 150 |  |  |
| 5 | CARPENTRY SERVICES (see Section C.2.8) |  |  |  |  |
| 5.1 | Supply and install 0.5mm IBR factory painted roof sheeting including nailing and insulation | m² | 100 |  |  |
| 5.2 | Supply and install clay/cement tiles including nailing | m² | 80 |  |  |
| 5.3 | Supply and install iron roof ridge | m | 100 |  |  |
| 5.4 | Supply and install roof ridge for clay/cement tiles | m | 25 |  |  |
| 5.5 | Supply and install metal gutter | m | 100 |  |  |
| 5.6 | Supply and install PVC ceiling including edge strips | m² | 150 |  |  |
| 5.7 | Supply and install 8mm particle board ceiling | m² | 100 |  |  |
| 5.8 | Supply and install sawn 50 x 50mm softwood blandering including supports | m | 300 |  |  |
| 5.9 | Supply and install wrought softwood 225x25 mm fascias board | m | 200 |  |  |
| 5.10 | Supply and install 100mm half round PVC gutter | m | 150 |  |  |
| 5.11 | Supply and install 150mm half round PVC gutter | m | 150 |  |  |
| 5.12 | Supply and install 100mm down pipes including connection to gutter ,end outlets and wall supports | m | 60 |  |  |
| 5.13 | Supply and install standard aluminum window complete with locking, flyscreen’s and 6mm glazing. | m² | 60 |  |  |
| 5.14 | Supply and install 45mm solid core flush doors | each | 30 |  |  |
| 5.15 | Supply and install 45mm hollow core flush doors | each | 15 |  |  |
| 5.16 | Supply and install 45mm mukwa/rosewood doors | each | 30 |  |  |
| 5.17 | Supply and install 3 lever mortice lock | each | 150 |  |  |
| 5.18 | Install government supplied dead bolt locks | each | 15 |  |  |
| 5.19 | Supply and install 150 X50mm rafters including painting with preservative | m | 200 |  |  |
| 5.20 | Supply and install 100 X 38mm rafters including painting with preservative and nailing | m | 200 |  |  |
| 5.21 | Supply and install 75 X50mm purlins including painting with preservative and nailing | m | 300 |  |  |
| 5.22 | Supply and Install shelving in cabinets using 18mm block boards | m² | 80 |  |  |
| 5.23 | Supply and Install double rod wooden curtain rails including supports size 2500m | each | 50 |  |  |
| 5.24 | Supply and Install double rod metal curtain rails including supports, | each | 50 |  |  |
| 5.25 | Supply and install suspended ceiling as 10mm rhinoboard or other equal approved plasterboard with skimmed plaster fixed already existing 50x50mm branders including joint tape and cornice | m² | 150 |  |  |
| 5.26 | Replace wooden framed screen door 2000 x900mm | each | 20 |  |  |
| 5.27 | Replace aluminum framed screen door 2000 x900mm | each | 20 |  |  |
| 5.28 | Replace fly screen including frame to windows 900x600mm | each | 60 |  |  |
| 5.29 | Supply and install door stopper | each | 200 |  |  |
| 5.30 | Supply and install parquet wood floor | m² | 200 |  |  |
| 5.31 | Supply and install 400x75x20mm teak wood floor | m² | 150 |  |  |
| 5.32 | Supply and install 400x75x20mm rosewood wood floor | m² | 100 |  |  |
| 5.33 | Supply and install 100mm x 20mm wood base board | m | 400 |  |  |
| 5.34 | Supply and install 75mm softwood cornice | m | 400 |  |  |
| 5.35 | Supply and install 40mm softwood cover strips | m | 250 |  |  |
| 5.36 | Supply install 100mm butt hinges complete with screws | each | 80 |  |  |
| 5.37 | Supply and install aluminum weather strips 900mm | each | 30 |  |  |
| 5.38 | Supply and install 6mm clear glass including putty | m² | 40 |  |  |
| 5.39 | Supply and install 3mm clear glass including putty | m² | 40 |  |  |
| 5.40 | Supply and install 6mm obscure glass including putty | m² | 15 |  |  |
| 5.41 | Supply and install 3mm obscure glass including putty | m² | 15 |  |  |
| 5.42 | Check and repair sticky hinges doors, drawers and sliding doors. Per house | lot | 14 |  |  |
| 5.43 | Clean chimneys and fireplaces per house | each | 10 |  |  |
| 5.44 | Replace 30mm granite counter tops 600mm | m | 25 |  |  |
| 5.45 | Replace cabinet hinges per house | each | 14 |  |  |
| 5.46 | Repair leaky roof using roof membrane /house | lot | 10 |  |  |
| 5.47 | Replace caulking around the bathtub and kitchen sink | m | 30 |  |  |
| 5.48 | Supply and install coat hooks | each | 20 |  |  |
| 5.49 | Supply and install soap holder | each | 20 |  |  |
| 5.50 | Supply and install toilet roll holder | each | 20 |  |  |
| 5.51 | Supply and install 25mm shower curtain rod complete with end brackets. | m | 25 |  |  |
| 5.52 | Supply and install insulation in the ceiling. | m² | 150 |  |  |
| 5.53 | Supply and install 1.6mm vinyl composition tile floor 300 x300mm including supply of adhesive. | m² | 80 |  |  |
| 5.54 | Supply and replace aluminum screen materials for doors or windows | m² | 80 |  |  |
| 5.55 | Supply and replace wooden door frame complete with trims | each | 20 |  |  |
| 5.56 | Supply and install quarter round wood mouldings | m | 100 |  |  |
| 6 | PLUMBING SERVICES (see Section C.2.5) |  |  |  |  |
| 6.1 | Check and test all plumbing fixtures and snake out all interior drain lines | lot | 8 |  |  |
| 6.2 | Replace 20mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.3 | Replace 12mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.4 | Replace kitchen double bowl sink | each | 8 |  |  |
| 6.5 | Replace swing kitchen faucet Cobra or similar quality | each | 10 |  |  |
| 6.6 | Replace P trap for kitchen sink | each | 20 |  |  |
| 6.7 | Replace wash hand basin of high quality | each | 15 |  |  |
| 6.8 | Supply and replace 12mm copper/flexi connector | each | 30 |  |  |
| 6.9 | Supply and replace 20mm copper/flexi connector | each | 30 |  |  |
| 6.10 | Supply and install 20mm CPVC gate valves | each | 150 |  |  |
| 6.11 | Supply and install 12mm CPVC gate valves | each | 150 |  |  |
| 6.12 | Supply and install connection from GI to CPVC 20mm | each | 40 |  |  |
| 6.13 | Supply and install connection from GI to CPVC 12mm | each | 40 |  |  |
| 6.14 | Supply and install 40mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.15 | Supply and install 50mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.16 | Supply and install 110mm PVC pipes complete with fittings | m | 400 |  |  |
| 6.17 | Supply and install telephone bath mixer 20mm | each | 20 |  |  |
| 6.18 | Supply and install 500x500 manhole cover | each | 15 |  |  |
| 6.19 | Supply and install shower valve and mixing assembly 20mm | each | 10 |  |  |
| 6.20 | Supply and install shower head | each | 20 |  |  |
| 6.21 | Supply and install toilet pan complete with cistern | each | 25 |  |  |
| 6.22 | Supply and install seat cover | each | 25 |  |  |
| 6.23 | Supply and install WHB mixer 12mm | each | 25 |  |  |
| 6.24 | Supply and install shower cubicle 1200x900 as supplied by Make a Home with tempered glass panels or similar | each | 10 |  |  |
| 6.25 | Supply and install bathtub 1700x600x450mm deep | each | 10 |  |  |
| 6.26 | Supply and install 6mm mirror complete with dome screws and caps | each | 20 |  |  |
| 6.27 | Chisel for piping in wall 50mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.28 | Chisel for piping in slab 70mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.29 | Chisel for piping through 100mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.30 | Chisel for piping through 150mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.31 | Chisel for piping through 200mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.32 | Supply and install 100 ltrs water heater | each | 20 |  |  |
| 6.33 | Service water heater by removing accumulation of scale, clean element with vinegar and re-install | lot | 10 |  |  |
| 6.34 | Supply and install 2KW heating element complete with thermostat. | each | 20 |  |  |
| 6.35 | Install valve labels | lot | 10 |  |  |
| 6.36 | Supply and install shut off valves 20mm | lot | 10 |  |  |
| 6.37 | Remove scale from mixers | lot | 10 |  |  |
| 7 | ELECTRICAL SERVICES (see Section C.2.6) |  |  |  |  |
| 7.1 | Replace existing light switches | each | 150 |  |  |
| 7.2 | Replace existing electrical outlets | each | 250 |  |  |
| 7.3 | Replace MCBs single pole 20Amps | each | 100 |  |  |
| 7.4 | Replace MCBs single pole 10Amps | each | 100 |  |  |
| 7.5 | Replace MCBs single pole 30Amps | each | 100 |  |  |
| 7.6 | Replace MCBs single pole 40Amps | each | 100 |  |  |
| 7.7 | Replace MCBs single pole 60Amps | each | 60 |  |  |
| 7.8 | Replace MCBs single pole 80Amps | each | 60 |  |  |
| 7.9 | Replace MCBs tripple pole 20Amps | each | 20 |  |  |
| 7.10 | Replace MCBs tripple pole 60Amps | each | 20 |  |  |
| 7.11 | Replace MCBs tripple pole 80Amps | each | 20 |  |  |
| 7.12 | Supply and install 1.5mm 2 cable red | m | 4000 |  |  |
| 7.13 | Supply and install 2.5mm 2 cable red | m | 4000 |  |  |
| 7.14 | Supply and install 4mm 2 cable red | m | 2500 |  |  |
| 7.15 | Supply and install 6mm 2 cable red | m | 1000 |  |  |
| 7.16 | supply and install 4 ft single fluorescent light fitting | each | 200 |  |  |
| 7.17 | supply and install 2 ft single fluorescent light fitting | each | 20 |  |  |
| 7.18 | supply and install 4 ft double fluorescent light fitting | each | 200 |  |  |
| 7.19 | supply and install 2 ft double fluorescent light fitting | each | 20 |  |  |
| 7.20 | supply and install recessed vapor barrier light fixture | each | 80 |  |  |
| 7.21 | Supply and install 6" spherical light fitting | each | 80 |  |  |
| 7.22 | Supply and install 8" spherical light fitting | each | 80 |  |  |
| 7.23 | Install government supplied chandelier | each | 20 |  |  |
| 7.24 | Install government supplied ceiling fan | each | 30 |  |  |
| 7.25 | Install government supplied GFCI socket outlets | each | 30 |  |  |
| 7.26 | Install government supplied door bell | each | 15 |  |  |
| 7.27 | Supply and install 20mm PVC electrical conduits | m | 1000 |  |  |
| 7.28 | Supply and install 25mm PVC electrical conduits | m | 1000 |  |  |
| 7.29 | Supply and install metal boxes 3"x3" | each | 300 |  |  |
| 7.30 | Supply and install metal boxes 6"x3" | each | 300 |  |  |
| 7.31 | Supply and install junction boxes complete with covers | each | 300 |  |  |
| 7.32 | Replace geyser switches | each | 30 |  |  |
| 7.33 | Supply and install light bulbs | each | 300 |  |  |
| 7.34 | supply and install lightening arrestors | each | 60 |  |  |
| 7.35 | Label distribution panel | lot | 10 |  |  |
| 7.36 | Install dead front panel | lot | 10 |  |  |
| 8 | PAINTING SERVICES (See Section C.2.1.4) |  |  |  |  |
| 8.1 | Clean old paint, repair plaster, prime and smooth surface, apply (1) coat of interior undercoat paint to walls and ceiling | m² | 2500 |  |  |
| 8.2 | Colored painting walls, two coats, (semi-gloss) paint, no surface preparation | m² | 4000 |  |  |
| 8.3 | Painting ceilings, two coats, (PVA) paint, no surface preparation | m² | 3000 |  |  |
| 8.4 | Paint, exterior oil 2 coat | m² | 800 |  |  |
| 8.5 | Paint, exterior latex, 2coat | m² | 2000 |  |  |
| 8.6 | Paint, exterior enamel,2coats | m² | 1000 |  |  |
| 8.7 | Paint, interior latex, 2 coat | m² | 2000 |  |  |
| 8.8 | Painting trim/baseboards, one coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.9 | Varnishing of woodwork, following surface preparation | m² | 1000 |  |  |
| 8.10 | Textured Surfaces preparatory work | m² | 1000 |  |  |
| 8.11 | Painting of textured surfaces, one coat, (latex semi-gloss, spray application incl. Floor coverings, etc.) | m² | 1000 |  |  |
| 8.12 | Prepare surface and apply ceiling texture (spray application incl. Floor coverings, etc.) | m² | 600 |  |  |
| 8.13 | Painting wood surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 600 |  |  |
| 8.14 | Painting metal surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 200 |  |  |
| 8.15 | Painting wood surfaces( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.16 | Painting metal surfaces ( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 9 | HVAC SERVICES (see Section C.2.7) |  |  |  |  |
| 9.1 | Install indoor Evaporator units. | each | 40 |  |  |
| 9.2 | Install outside condensing units | each | 40 |  |  |
| 9.3 | Install refrigeration lines/pipes between the inside and outside units. The refrigeration lines/pipes between the inside and outside units must be installed following a route and in a manner acceptable to the Contracting Officer Representative. Insulate all pipes with Armaflex | each | 40 |  |  |
| 9.4 | Install all pipes in Trunkings and provide for Air-conditioning drain. | each | 40 |  |  |
| 9.5 | Install thermostat holder. The location where the thermostat will be installed will be coordinated with the contracting Officer Representative. | each | 40 |  |  |
| 9.6 | Provide for an Isolation switch for the indoor and outdoor unit | each | 40 |  |  |
| 9.7 | Install electrical power and signal cable between indoor and outdoor unit. | each | 40 |  |  |
| 9.8 | The new AC units must be tested for proper operation. The contractor must demonstrate to the Contracting Officer Representatives that the system functions properly before the project will be accepted. | each | 40 |  |  |
| 9.9 | Carry out full service of the existing ACs as described in C.2.4 (c ) | each | 40 |  |  |
|  | Total of all line-item prices: |  |  |  |  |
|  | Third Option year total |  |  |  |  |

*m² – square meter

The estimated amounts are based on total estimated Government requirements.  This means that if more than one award is made, the estimated amount of work awarded under task order(s) to any single contractor will be less than the amount shown.

B.3.7	FOURTH OPION YEAR PRICES

| Item | Description | Unit | Quantity | Rate | Amount |
| --- | --- | --- | --- | --- | --- |
| 1 | DEMOLITION SERVICES |  |  |  |  |
| 1.1 | Demolish existing concrete slab, remove debris from site and cart away to contractor's dump site(average thickness 150mm) | m³ | 7 |  |  |
| 1.2 | Demolish existing masonry wall including plaster, remove debris from site and cart away to contractor's dump site | m² | 70 |  |  |
| 1.3 | Carefully remove roof covering and all damaged purlin and roof structure, remove debris from site and cart away to contractor's dump site | m² | 60 |  |  |
| 1.4 | Remove existing gutters ,remove debris from and cart away to contractors dump site | m | 150 |  |  |
| 1.5 | Remove existing fascial board, remove debris from site and cart away to contractor’s dump site | m | 150 |  |  |
| 1.6 | Remove all existing wall tiles, remove debris from site and cart away to contractor's dump site | m | 60 |  |  |
| 1.7 | Remove all existing floor covering, remove debris from site and cart away to contractor's dump site | m² | 200 |  |  |
| 1.8 | Remove existing door frames including lintol , remove debris and hand over frame to client or cart away to contractor’s dump site | each | 15 |  |  |
| 1.9 | Remove existing window frames including lintol , remove debris and hand over frame to client or cart away to contractor's dump site | lot | 7 |  |  |
| 1.10 | Remove existing bathtub ,wash hand basin and toilet pan, clean drain and hand over to the COR | lot | 8 |  |  |
| 1.11 | Remove all plumbing piping , remove debris and cart away to contractor’s dump site | lot | 8 |  |  |
| 1.12 | Removing existing particle board/gypsum board ceiling including blundering, remove debris and cart away. | m² | 150 |  |  |
| 1.13 | Remove existing wall cabinets and hand over to the COR | lot | 7 |  |  |
| 1.14 | Remove existing curtain rails and supports. Hand over to the COR | m | 100 |  |  |
| 1.15 | Carefully remove all distribution panel boards including all cabling and take away from site | lot | 7 |  |  |
| 1.16 | Carefully remove all electrical light fittings including switches and cabling and take away from site | lot | 7 |  |  |
| 1.17 | Carefully remove all sockets including all cabling and take away from site | lot | 7 |  |  |
| 2 | CONCRETE SERVICES |  |  |  |  |
| 2.1 | Supply and cast plain concrete grade 20/20 mm aggregate. | m³ | 10 |  |  |
| 2.2 | Supply and cast vibrated reinforced concrete grade 25/20 mm aggregate. | m³ | 8 |  |  |
| 2.3 | Supply and lay deformed steel bars reinforcement (varies sizes) | kg | 100 |  |  |
| 2.4 | Supply and lay steel mesh fabric reinforcement conforce 257 allowing 200mm lap at joints | m² | 20 |  |  |
| 2.5 | Supply and lay steel mesh fabric reinforcement conforce 86 allowing 200mm lap at joints | m² | 25 |  |  |
| 2.6 | Formworks for sides of columns, steps edges of the beds | m² | 120 |  |  |
| 2.7 | Repair crack concrete screed chip off 25mm wide V joint seal with cement grout | m | 60 |  |  |
| 3 | SITE SERVICES |  |  |  |  |
| 3.1 | Clear site of works of shrubs, bushes and trees | m² | 50 |  |  |
| 3.2 | Excavate around foundation not exceeding 1m deep | m³ | 10 |  |  |
| 3.3 | Excavate to remove top soil and load and cart away to contractors tipping site average depth 150mm | m² | 70 |  |  |
| 3.4 | load and cart away surplus spoil to contractor’s dump site | m³ | 60 |  |  |
| 3.5 | Backfill and compact in layers not exceeding 150mm | m³ | 90 |  |  |
| 3.6 | Supply and install 500 gauge polythene laid under surface beds | m² | 90 |  |  |
| 3.7 | Apply approved ant termite treatment | m² | 90 |  |  |
| 4 | MASONRY SERVICES (See section C.2.11) |  |  |  |  |
| 4.1 | Erect hollow block walling (3.5N/m2 crushing strength) in cement mortar allow for brick force reinforcement every 3 courses |  |  |  |  |
| 4.1.1 | 200mm walls | m² | 60 |  |  |
| 4.1.2 | 150mm walls | m² | 80 |  |  |
| 4.1.3 | 100mm walls | m² | 70 |  |  |
| 4.2 | Erect Solid block/brick walling (5.0N/m2 crushing strength) in cement mortar and allowing for brick force reinforcement every 3 courses |  |  |  |  |
| 4.2.1 | 200mm walls | m² | 40 |  |  |
| 4.2.2 | 150mm walls | m² | 50 |  |  |
| 4.2.3 | 100mm walls | m² | 30 |  |  |
| 4.3 | Cement /sand plaster |  |  |  |  |
| 4.3.1 | Cement/sand (1:4) external rendering 20mm thick in wood float finish | m² | 100 |  |  |
| 4.3.2 | Cement/sand (1:3) internal rendering 20mm thick in steel trowelled smooth finish | m² | 100 |  |  |
| 4.3.3 | Plaster to reveal and returns | m | 100 |  |  |
| 4.4 | Beam filling between wall and roof | m | 100 |  |  |
| 4.5 | Supply and install 14g standard pressed steel door frame, double rebated including hinges, masonry, jamps and striking plate. | each | 15 |  |  |
| 4.6 | Supply and install standard metal window frame size 1200x900mm complete with handle and stays | each | 15 |  |  |
| 4.7 | Supply and install standard metal window frame size 2400x900mm complete with handle and stays | each | 8 |  |  |
| 4.8 | Supply and install standard metal window frame size 900x600mm complete with handle and stays | each | 8 |  |  |
| 4.9 | Supply and install standard metal window frame size 1800x900mm complete with handle and stays | each | 8 |  |  |
| 4.10 | Supply and apply gypsum plaster in one coat skimming finish with a steel trowel | m² | 100 |  |  |
| 4.11 | Supply and install ceramic floor tiles (Grade AAA). Including grouting and sealing. | m² | 100 |  |  |
| 4.12 | Supply and install porcelain floor tiles. (Grade AAA) including grouting and grout sealing | m² | 100 |  |  |
| 4.13 | Supply and install ceramic wall tiles(Grade AAA) including grouting and sealing | m² | 300 |  |  |
| 4.14 | Cast and install 40mm floor screed in cement/ sand mix (1:3) | m² | 150 |  |  |
| 5 | CARPENTRY SERVICES (see Section C.2.8) |  |  |  |  |
| 5.1 | Supply and install 0.5mm IBR factory painted roof sheeting including nailing and insulation | m² | 100 |  |  |
| 5.2 | Supply and install clay/cement tiles including nailing | m² | 80 |  |  |
| 5.3 | Supply and install iron roof ridge | m | 100 |  |  |
| 5.4 | Supply and install roof ridge for clay/cement tiles | m | 25 |  |  |
| 5.5 | Supply and install metal gutter | m | 100 |  |  |
| 5.6 | Supply and install PVC ceiling including edge strips | m² | 150 |  |  |
| 5.7 | Supply and install 8mm particle board ceiling | m² | 100 |  |  |
| 5.8 | Supply and install sawn 50 x 50mm softwood blandering including supports | m | 300 |  |  |
| 5.9 | Supply and install wrought softwood 225x25 mm fascias board | m | 200 |  |  |
| 5.10 | Supply and install 100mm half round PVC gutter | m | 150 |  |  |
| 5.11 | Supply and install 150mm half round PVC gutter | m | 150 |  |  |
| 5.12 | Supply and install 100mm down pipes including connection to gutter ,end outlets and wall supports | m | 60 |  |  |
| 5.13 | Supply and install standard aluminum window complete with locking, flyscreen’s and 6mm glazing. | m² | 60 |  |  |
| 5.14 | Supply and install 45mm solid core flush doors | each | 30 |  |  |
| 5.15 | Supply and install 45mm hollow core flush doors | each | 15 |  |  |
| 5.16 | Supply and install 45mm mukwa/rosewood doors | each | 30 |  |  |
| 5.17 | Supply and install 3 lever mortice lock | each | 150 |  |  |
| 5.18 | Install government supplied dead bolt locks | each | 15 |  |  |
| 5.19 | Supply and install 150 X50mm rafters including painting with preservative | m | 200 |  |  |
| 5.20 | Supply and install 100 X 38mm rafters including painting with preservative and nailing | m | 200 |  |  |
| 5.21 | Supply and install 75 X50mm purlins including painting with preservative and nailing | m | 300 |  |  |
| 5.22 | Supply and Install shelving in cabinets using 18mm block boards | m² | 80 |  |  |
| 5.23 | Supply and Install double rod wooden curtain rails including supports size 2500m | each | 50 |  |  |
| 5.24 | Supply and Install double rod metal curtain rails including supports, | each | 50 |  |  |
| 5.25 | Supply and install suspended ceiling as 10mm rhinoboard or other equal approved plasterboard with skimmed plaster fixed already existing 50x50mm branders including joint tape and cornice | m² | 150 |  |  |
| 5.26 | Replace wooden framed screen door 2000 x900mm | each | 20 |  |  |
| 5.27 | Replace aluminum framed screen door 2000 x900mm | each | 20 |  |  |
| 5.28 | Replace fly screen including frame to windows 900x600mm | each | 60 |  |  |
| 5.29 | Supply and install door stopper | each | 200 |  |  |
| 5.30 | Supply and install parquet wood floor | m² | 200 |  |  |
| 5.31 | Supply and install 400x75x20mm teak wood floor | m² | 150 |  |  |
| 5.32 | Supply and install 400x75x20mm rosewood wood floor | m² | 100 |  |  |
| 5.33 | Supply and install 100mm x 20mm wood base board | m | 400 |  |  |
| 5.34 | Supply and install 75mm softwood cornice | m | 400 |  |  |
| 5.35 | Supply and install 40mm softwood cover strips | m | 250 |  |  |
| 5.36 | Supply install 100mm butt hinges complete with screws | each | 80 |  |  |
| 5.37 | Supply and install aluminum weather strips 900mm | each | 30 |  |  |
| 5.38 | Supply and install 6mm clear glass including putty | m² | 40 |  |  |
| 5.39 | Supply and install 3mm clear glass including putty | m² | 40 |  |  |
| 5.40 | Supply and install 6mm obscure glass including putty | m² | 15 |  |  |
| 5.41 | Supply and install 3mm obscure glass including putty | m² | 15 |  |  |
| 5.42 | Check and repair sticky hinges doors, drawers and sliding doors. Per house | lot | 14 |  |  |
| 5.43 | Clean chimneys and fireplaces per house | each | 10 |  |  |
| 5.44 | Replace 30mm granite counter tops 600mm | m | 25 |  |  |
| 5.45 | Replace cabinet hinges per house | each | 14 |  |  |
| 5.46 | Repair leaky roof using roof membrane /house | lot | 10 |  |  |
| 5.47 | Replace caulking around the bathtub and kitchen sink | m | 30 |  |  |
| 5.48 | Supply and install coat hooks | each | 20 |  |  |
| 5.49 | Supply and install soap holder | each | 20 |  |  |
| 5.50 | Supply and install toilet roll holder | each | 20 |  |  |
| 5.51 | Supply and install 25mm shower curtain rod complete with end brackets. | m | 25 |  |  |
| 5.52 | Supply and install insulation in the ceiling. | m² | 150 |  |  |
| 5.53 | Supply and install 1.6mm vinyl composition tile floor 300 x300mm including supply of adhesive. | m² | 80 |  |  |
| 5.54 | Supply and replace aluminum screen materials for doors or windows | m² | 80 |  |  |
| 5.55 | Supply and replace wooden door frame complete with trims | each | 20 |  |  |
| 5.56 | Supply and install quarter round wood mouldings | m | 100 |  |  |
| 6 | PLUMBING SERVICES (see Section C.2.5) |  |  |  |  |
| 6.1 | Check and test all plumbing fixtures and snake out all interior drain lines | lot | 8 |  |  |
| 6.2 | Replace 20mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.3 | Replace 12mm CPVC water pipe complete with fittings fixed approved solvent | m | 500 |  |  |
| 6.4 | Replace kitchen double bowl sink | each | 8 |  |  |
| 6.5 | Replace swing kitchen faucet Cobra or similar quality | each | 10 |  |  |
| 6.6 | Replace P trap for kitchen sink | each | 20 |  |  |
| 6.7 | Replace wash hand basin of high quality | each | 15 |  |  |
| 6.8 | Supply and replace 12mm copper/flexi connector | each | 30 |  |  |
| 6.9 | Supply and replace 20mm copper/flexi connector | each | 30 |  |  |
| 6.10 | Supply and install 20mm CPVC gate valves | each | 150 |  |  |
| 6.11 | Supply and install 12mm CPVC gate valves | each | 150 |  |  |
| 6.12 | Supply and install connection from GI to CPVC 20mm | each | 40 |  |  |
| 6.13 | Supply and install connection from GI to CPVC 12mm | each | 40 |  |  |
| 6.14 | Supply and install 40mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.15 | Supply and install 50mm PVC waste pipes complete with fitting. | m | 200 |  |  |
| 6.16 | Supply and install 110mm PVC pipes complete with fittings | m | 400 |  |  |
| 6.17 | Supply and install telephone bath mixer 20mm | each | 20 |  |  |
| 6.18 | Supply and install 500x500 manhole cover | each | 15 |  |  |
| 6.19 | Supply and install shower valve and mixing assembly 20mm | each | 10 |  |  |
| 6.20 | Supply and install shower head | each | 20 |  |  |
| 6.21 | Supply and install toilet pan complete with cistern | each | 25 |  |  |
| 6.22 | Supply and install seat cover | each | 25 |  |  |
| 6.23 | Supply and install WHB mixer 12mm | each | 25 |  |  |
| 6.24 | Supply and install shower cubicle 1200x900 as supplied by Make a Home with tempered glass panels or similar | each | 10 |  |  |
| 6.25 | Supply and install bathtub 1700x600x450mm deep | each | 10 |  |  |
| 6.26 | Supply and install 6mm mirror complete with dome screws and caps | each | 20 |  |  |
| 6.27 | Chisel for piping in wall 50mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.28 | Chisel for piping in slab 70mm deep for pipes up 50mm | lot | 10 |  |  |
| 6.29 | Chisel for piping through 100mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.30 | Chisel for piping through 150mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.31 | Chisel for piping through 200mm wall for pipes up 110mm | lot | 10 |  |  |
| 6.32 | Supply and install 100 ltrs water heater | each | 20 |  |  |
| 6.33 | Service water heater by removing accumulation of scale, clean element with vinegar and re-install | lot | 10 |  |  |
| 6.34 | Supply and install 2KW heating element complete with thermostat. | each | 20 |  |  |
| 6.35 | Install valve labels | lot | 10 |  |  |
| 6.36 | Supply and install shut off valves 20mm | lot | 10 |  |  |
| 6.37 | Remove scale from mixers | lot | 10 |  |  |
| 7 | ELECTRICAL SERVICES (see Section C.2.6) |  |  |  |  |
| 7.1 | Replace existing light switches | each | 150 |  |  |
| 7.2 | Replace existing electrical outlets | each | 250 |  |  |
| 7.3 | Replace MCBs single pole 20Amps | each | 100 |  |  |
| 7.4 | Replace MCBs single pole 10Amps | each | 100 |  |  |
| 7.5 | Replace MCBs single pole 30Amps | each | 100 |  |  |
| 7.6 | Replace MCBs single pole 40Amps | each | 100 |  |  |
| 7.7 | Replace MCBs single pole 60Amps | each | 60 |  |  |
| 7.8 | Replace MCBs single pole 80Amps | each | 60 |  |  |
| 7.9 | Replace MCBs tripple pole 20Amps | each | 20 |  |  |
| 7.10 | Replace MCBs tripple pole 60Amps | each | 20 |  |  |
| 7.11 | Replace MCBs tripple pole 80Amps | each | 20 |  |  |
| 7.12 | Supply and install 1.5mm 2 cable red | m | 4000 |  |  |
| 7.13 | Supply and install 2.5mm 2 cable red | m | 4000 |  |  |
| 7.14 | Supply and install 4mm 2 cable red | m | 2500 |  |  |
| 7.15 | Supply and install 6mm 2 cable red | m | 1000 |  |  |
| 7.16 | supply and install 4 ft single fluorescent light fitting | each | 200 |  |  |
| 7.17 | supply and install 2 ft single fluorescent light fitting | each | 20 |  |  |
| 7.18 | supply and install 4 ft double fluorescent light fitting | each | 200 |  |  |
| 7.19 | supply and install 2 ft double fluorescent light fitting | each | 20 |  |  |
| 7.20 | supply and install recessed vapor barrier light fixture | each | 80 |  |  |
| 7.21 | Supply and install 6" spherical light fitting | each | 80 |  |  |
| 7.22 | Supply and install 8" spherical light fitting | each | 80 |  |  |
| 7.23 | Install government supplied chandelier | each | 20 |  |  |
| 7.24 | Install government supplied ceiling fan | each | 30 |  |  |
| 7.25 | Install government supplied GFCI socket outlets | each | 30 |  |  |
| 7.26 | Install government supplied door bell | each | 15 |  |  |
| 7.27 | Supply and install 20mm PVC electrical conduits | m | 1000 |  |  |
| 7.28 | Supply and install 25mm PVC electrical conduits | m | 1000 |  |  |
| 7.29 | Supply and install metal boxes 3"x3" | each | 300 |  |  |
| 7.30 | Supply and install metal boxes 6"x3" | each | 300 |  |  |
| 7.31 | Supply and install junction boxes complete with covers | each | 300 |  |  |
| 7.32 | Replace geyser switches | each | 30 |  |  |
| 7.33 | Supply and install light bulbs | each | 300 |  |  |
| 7.34 | supply and install lightening arrestors | each | 60 |  |  |
| 7.35 | Label distribution panel | lot | 10 |  |  |
| 7.36 | Install dead front panel | lot | 10 |  |  |
| 8 | PAINTING SERVICES (See Section C.2.1.4) |  |  |  |  |
| 8.1 | Clean old paint, repair plaster, prime and smooth surface, apply (1) coat of interior undercoat paint to walls and ceiling | m² | 2500 |  |  |
| 8.2 | Colored painting walls, two coats, (semi-gloss) paint, no surface preparation | m² | 4000 |  |  |
| 8.3 | Painting ceilings, two coats, (PVA) paint, no surface preparation | m² | 3000 |  |  |
| 8.4 | Paint, exterior oil 2 coat | m² | 800 |  |  |
| 8.5 | Paint, exterior latex, 2coat | m² | 2000 |  |  |
| 8.6 | Paint, exterior enamel,2coats | m² | 1000 |  |  |
| 8.7 | Paint, interior latex, 2 coat | m² | 2000 |  |  |
| 8.8 | Painting trim/baseboards, one coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.9 | Varnishing of woodwork, following surface preparation | m² | 1000 |  |  |
| 8.10 | Textured Surfaces preparatory work | m² | 1000 |  |  |
| 8.11 | Painting of textured surfaces, one coat, (latex semi-gloss, spray application incl. Floor coverings, etc.) | m² | 1000 |  |  |
| 8.12 | Prepare surface and apply ceiling texture (spray application incl. Floor coverings, etc.) | m² | 600 |  |  |
| 8.13 | Painting wood surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 600 |  |  |
| 8.14 | Painting metal surfaces, two coat, (lead-free) paint, gloss finish, following surface preparation | m² | 200 |  |  |
| 8.15 | Painting wood surfaces( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 8.16 | Painting metal surfaces ( narrow surfaces not exceeding 300mm wide),two coat, (lead-free) paint, gloss finish, following surface preparation | m | 1000 |  |  |
| 9 | HVAC SERVICES (see Section C.2.7) |  |  |  |  |
| 9.1 | Install indoor Evaporator units. | each | 40 |  |  |
| 9.2 | Install outside condensing units | each | 40 |  |  |
| 9.3 | Install refrigeration lines/pipes between the inside and outside units. The refrigeration lines/pipes between the inside and outside units must be installed following a route and in a manner acceptable to the Contracting Officer Representative. Insulate all pipes with Armaflex | each | 40 |  |  |
| 9.4 | Install all pipes in Trunkings and provide for Air-conditioning drain. | each | 40 |  |  |
| 9.5 | Install thermostat holder. The location where the thermostat will be installed will be coordinated with the contracting Officer Representative. | each | 40 |  |  |
| 9.6 | Provide for an Isolation switch for the indoor and outdoor unit | each | 40 |  |  |
| 9.7 | Install electrical power and signal cable between indoor and outdoor unit. | each | 40 |  |  |
| 9.8 | The new AC units must be tested for proper operation. The contractor must demonstrate to the Contracting Officer Representatives that the system functions properly before the project will be accepted. | each | 40 |  |  |
| 9.9 | Carry out full service of the existing ACs as described in C.2.4 (c ) | each | 40 |  |  |
|  | Total of all line-item prices: |  |  |  |  |
|  | Fourth Option year total |  |  |  |  |

*m² – square meter

The estimated amounts are based on total estimated Government requirements.  This means that if more than one award is made, the estimated amount of work awarded under task order(s) to any single contractor will be less than the amount shown.

### B.3.4	GRAND TOTAL PRICE FOR BASE YEAR PLUS FOUR OPTION 			YEARS

| Base Year Total: |  |
| --- | --- |
| First Option Year Total: |  |
| Second Option Year Total: |  |
| Third Option Year Total: |  |
| Fourth Option Year Total: |  |
| Grand Total Price for all Years: |  |

B.4	ORDERING - The Government shall issue task orders for ordering all services under this contract.  Task orders may be issued from the effective date of the contract until the end of the "Period of Performance."  All task orders are subject to the terms and conditions of this contract.  This contract shall take precedence in the event of conflict with any task order.

B.4.1 	ISSUANCE OF TASK ORDERS - The Contracting Officer may issue task orders orally but will be confirm them in writing within three days.

# B.4.2	SURVEY OF PROPERTY - Before performing work, the Contractor shall survey the property and verify the work required against the task, to determine if any discrepancies exist.  The Contractor shall be responsible for any errors that might have been avoided by such a survey/review.  The Contractor shall immediately report any discrepancies to the COR or the Contracting Officer and shall not begin work until such matters are resolved.

# B.4.3 	CONTENTS OF TASK ORDERS - The Contracting Officer shall issue task orders for make-ready services on an as-needed basis.  See the sample task order at Section J, Exhibit 2.  Task orders shall include:

- Date of order

- Contract number

- Order number

# Location of property

- Amount of work (square meters or linear meters)

- Point of contact for questions

- Description of services to be performed

# B.4.4	COMPLETION DATE – The Contractor shall complete all services on individual housing units within twenty one (21) days of receipt of a task order.  The time period specified above shall not begin until the Contractor is afforded reasonable access to the work site.

The time period specified above may be shortened if mutually agreed to by the contractor and the Government.

The completion date is fixed and may be extended only by a written modification signed by the Contracting Officer.

B.4.5      ISSUANCE OF TASK ORDERS – As the need for services arises, the Government will develop a price estimate.  If the estimate does not exceed US $10,000, the Government will follow the procedures in paragraph (1) below.  If the estimate exceeds US $10,000, the Government will follow the procedures in paragraph (2) below.

(1)  Orders not exceeding US $10,000 - The Government will select a contractor for issuance of the order.  This decision will be based on the Government's best interests, which may include factors such as estimated price and past performance record.

(2) Orders exceeding US $10,000 - Unless one of the exceptions in paragraph (4), below, applies, the Contracting Officer will determine which Contractor’s prices will result in the lowest price for the individual order, the Government will make its award selection based upon the prices set forth in the contract times the estimated quantity for each requirement and past performance information gained as a result of contractor performance under this contract.

(3) Regardless of whether the procedures in paragraph (1) or (2) above were followed, selection of contractors shall not be protestable to GAO under Subpart 33.1 of the Federal Acquisition Regulation, except on the grounds that the order increases the scope, period, or maximum value of the contract.  However, the Department of State does have an Acquisition Ombudsman who will review complaints by contractors to ensure that all contractors are afforded a fair opportunity to be considered for these task orders, pursuant to the procedures for award of task orders established herein.

(4) Exceptions to the procedures in paragraph (2) above:

(a)          The agency need for the required services is of such urgency that providing such competitive opportunity would result in unacceptable delays;

(b)          The order should be issued on a sole-source basis in the interest of economy and efficiency as a logical follow-on to an order already issued under the contract, provided that all awardees were given a fair opportunity to be considered for the original order.

(c)           It is necessary to place an order to satisfy a minimum guarantee

SECTION C - DESCRIPTION/SPECIFICATIONS/WORK STATEMENT

C.1	INTRODUCTION

C.1.1	GENERAL - The U.S Embassy Lusaka requires a make-ready service contractor to perform task orders on US Government owned and leased properties.  The Contractor shall furnish managerial, administrative and direct operational personnel to accomplish all work as required.

C.1.2	ENGLISH SPEAKING REPRESENTATIVE - The Contractor shall designate an English speaking representative who shall supervise the Contractor's workforce and be the Contractor's liaison with the Government.

The designated representative shall be located on site in an office designated by the Contracting Officer during normal working hours (see Section F.8) and shall have supervision as its sole function during the times while on duty.  The Contractor's employees shall be on site only for contractual duties and not for any other business or purposes.

C.1.2.	PERSONNEL - The Contractor shall be responsible for providing qualified technicians for each trade with relevant experience to perform make-ready services for task orders issued under this contract.  Helper positions do not need to meet the experience requirement.

C.1.3	DEFINITIONS (see also FAR clause 52.202-1, Alt. 1 [APR 1994], cited 	in I.1)

HVAC - Heating Ventilation and Air Conditioning.

Make-ready Services – Preparation of residential units for occupancy, including all items in this contract.

C.2	STANDARDS

C.2.1	APPLICABLE PAINTING STANDARDS AND PAINT 	SPECIFICATIONS

C.2.1.1	  LOCAL/INDUSTRY PAINTING STANDARDS

Painting and preparatory work shall be in accordance with South African Bureau of Standards (SABS), and the instructions given below.  In cases where local standards and those listed in this contract are in conflict, the stricter of the two shall apply.

# C.2.1.2   PAINT SPECIFICATIONS

Paint used shall all be lead free. It shall either be a latex or semi-gloss or high gloss paint and the color shall match the existing or as specified by the Contracting Officer.

# C.2.1.3	  PREPARATION AND PROTECTION OF WORK AREA

Painting shall not disturb or damage any fixed property (including light fixtures, floors, carpets, or windows).  The Contractor shall move, protect, and return such property to its original position.

The Contractor shall remove furnishings (such as furniture, rugs) first or protect them by protective covering.  The Contractor shall also protect floors from soiling and paint spills. The Contractor shall not wash wooden floors under any circumstances.  To protect floors (of all types) from damage, the Contractor shall use a suitable protective cover and provide ladders and scaffolding with clean rubber shoes or similar protection devices.

If the Contractor spills any paint, or in any way soils the floors, a specialist floor finishing company at the Contractor’s expense shall perform the clean up.  After completion of the painting work, the Contractor shall return all furnishings to their original position, and clean the work area free of litter and debris.

C.2.1.4	   TECHNICAL SPECIFICATIONS FOR PAINTING WORK

- INTERIOR AND EXTERIOR PAINTING

Paint surfaces as directed by the task order.  Match paint to similar adjacent materials or surfaces.

- "Paint" includes coating systems materials, primers, emulsions, enamels, stains, sealers and fillers, and other applied materials whether used as prime, intermediate or finish coats.

- Product Data:  The Contractor shall submit manufacturer's technical information, label analysis, and application instructions for each paint material proposed for use to the COR, prior to starting work.  As an attachment, list each material and cross-reference specific coating and finish system and application.  Identify each material by the manufacturer's catalog number and general classification.

- Single Source Responsibility:  Provide primers and undercoat paint produced by the same manufacturer as the finish coats.

- Material Quality:  Provide the manufacturer's best quality trade sale type paint material.  Paint material containers not displaying manufacturer's product identification will not be acceptable.

- Deliver materials to the job site in manufacturer's original, unopened packages and containers bearing manufacturer's name and label with trade name and manufacturer's instructions.

- Store materials not in use in tightly covered containers in a well-ventilated area at a minimum ambient temperature of 45 degrees F (7 degrees C). Protect from freezing.  Keep storage area neat and orderly.  Remove oily rags and waste daily.

- Project Conditions:  Do not apply paint when the relative humidity exceeds 85 percent, at temperatures less than 5 degrees F (3 degrees C) above the dew point, or to damp or wet surfaces.  Apply paint only in temperatures in accordance with manufacturer's specifications.

- Examine substrates and conditions under which painting will be performed for compliance with requirements.  Do not begin application until unsatisfactory conditions have been corrected.

- Preparation:  Remove hardware and hardware accessories, plates, light fixtures, and items in place that are not to be painted, or provide protection such as taping prior to surface preparation and painting (taping includes windows, door jams, etc.).

(10) Clean and prepare surfaces to be painted following manufacturer's instructions before applying paint or surface treatments.  Remove oil, dust, and direct, loose rust, mildew, peeling paint or other contamination to ensure good adhesion.  In some cases, the Contractor may be requested to remove all existing coats of paint and sealers if prior paint application is showing signs of improper adhesion, such as peeling, or chipping.  All surfaces must be clean and dry.  Schedule cleaning and painting so dust and other contaminants will not fall on wet, newly painted surfaces.

(11) Notify the Contracting Officer or COR of problems anticipated for any minor preparatory work required, such as but not limited to, filling nail holes, cleaning surfaces to be painted, and priming any requisite areas.  Plan preparatory work as most units in residential areas will have nail holes or areas that will need to be primed or sealed.  Replace all electrical switches and plugs with new covers after painting.

(12) Materials Preparation:  Mix and prepare paint following manufacturer's directions.

(13) Application:  Apply paint following manufacturer's directions.  Use applicators and techniques best suited for substrate and type of material being applied.  Do not paint over dirt, rust, scale, grease, moisture, scuffed surfaces, or conditions detrimental to formation of a durable paint film.

- Unless otherwise specified, the contractor is to use a high quality semi-gloss latex paint (containing no lead or mercury) for all kitchens, baths, laundry areas, doorframes, and window frames.  A flat or satin flat latex base paint (containing no lead or mercury) is to be used in the remainder of the unit.  The color to be used must be consistent with the balance of the room, which will normally be off-white.  Contractor shall provide samples of the color of the type of material to be painted before actual paint date is scheduled.

- On exterior surfaces, apply a high quality exterior grade latex base paint that matches as closely as possible to the existing color on the exterior of the property, or a color as otherwise specified by the COR.  Before painting, scrape, sand, fill and prime the surface with a latex base primer.  The Contractor should plan on extensive preparatory work before painting.  Do not apply exterior paint in snow, rain, fog or mist; or when the relatively humidity exceeds 85 percent; or to damp or wet surfaces.

- Provide finish coats that are compatible with primers used.

- The number of coats and film thickness required is the same regardless of application method.  Do not apply succeeding coats until previous coat has cured.  Sand between applications where required to produce a smooth, even surface.

- Apply additional coats when undercoats or other conditions show through final coat, until paint film is of uniform finish, color, and appearance.

(14) Scheduling Painting:  Apply first coat to surfaces that have been cleaned, pretreated or otherwise prepared for painting as soon as practicable, and before subsequent surface deterioration.  Allow sufficient time between successive coats to permit proper drying.  Do not re-coat until paint has dried.

(15) Minimum Coating Thickness:  Apply materials at the manufacturer's recommended spreading rate.  Provide total dry film thickness of the system as recommended by the manufacturer.

(16) Prime Coats:  Before application of finish coats, apply a prime coat as recommended by the manufacturer to material required to be painted or finished, and has not been prime coated.

(17) Brush Application:  Brush out and work brush coats into surfaces in an even film.  Eliminate cloudiness, spotting, laps, brush marks, runs, sags, ropiness, or other surface imperfections.  Draw neat glass lines and color breaks.

(18) Apply primers and first coats by brush unless manufacturer's instructions permit use of mechanical applicators.

(19) Mechanical Applications:  Use mechanical methods for paint application when permitted by manufacturer's recommendations, governing ordinances, and trade union regulations.

(20) Wherever spray application is used, apply each coat to provide the equivalent hiding of brush-applied coats. Do not double-back with spray equipment to build up film thickness of two coats in one pass, unless recommended by the manufacturer.

(21) Upon completion of painting, clean glass and paint-spattered surfaces.  Remove spattered paint by washing, scraping or other methods, using care not to scratch or damage adjacent finished surfaces.

(22) Remove temporary protective wrappings after completion of painting operations.

- DRYWALL/PLASTER REPAIR

Patch defective drywall with a similar thickness and fire rated drywall.  Joints must be taped in a manner so they are not readily visible.  The patch must be textured with a texture consistent with the rest of the surface being patched.  All nail heads must be set and spackled.  Joints must be taped and covered with a joint compound.  Spackled nail heads and tape joints must be sanded smooth and all dust removed prior to paining.  Exterior surfaces must be spackled with exterior grade compounds.

- TEXTURE ONLY - WALLS

Occasionally, the Government may require a wall to be textured that has not previously been textured.  The Contractor shall prepare the wall by filling and sanding any small holes or cracks with a suitable "non-shrinking" material.  After preparatory work, the Contractor shall furnish and apply a texture type material.  If any other walls within that room are textured, the texture material shall closely match the texture of any other existing textured walls in that room.  The minimum assignment for this requirement will be one room within a unit.

- TEXTURE ONLY - CEILING

Occasionally, the Government may require that a ceiling be textured that has not previously been textured.  The Contractor shall prepare the ceiling by filling and sanding any small holes or cracks with a suitable "non-shrinking" material.  After preparatory work, the Contractor shall furnish and apply an "acoustic" type texture.  The minimum assignment for this requirement will be one room within a unit.

- PAINT EXTERIOR TRIM

Apply a high quality exterior grade latex base paint that matches as closely as possible the existing color on the exterior trim of the property, or a color as specified by the COR.  The trim is to be scraped, sanded, filled, and primed with a latex base primer, prior to painting.  The Contractor should plan on extensive preparatory work prior to painting.  The specifications for exterior paint apply, unless otherwise specified.

- REMOVE WALL COVERING

By task order, remove the designated wall covering (such as wallpaper, cork, mirror, and tile).  After removing the wall covering the area shall be cleaned and made ready for painting.  The Contractor shall remove and properly dispose of the old wall covering.

- PLASTER

Repair any damaged interior or exterior plaster as directed by the COR.  The plaster material shall be of a similar material that matches as closely as possible the existing plaster in texture and color.

- STUCCO

Repair any damaged stucco and remove any loose stucco before applying paint.

C.2.2	PLUMBING SERVICES

The Contractor shall perform the following plumbing inspection and repairs and use the checklist in Section J, Exhibit 4.

- Inspect all plumbing work including:

- pipes, ducts, valves, dampers, fittings, waste water and sewer lines, traps, catch basins, hot water heaters, toilet fixtures, plugs, chains, hoses, down-spouts, and gutters for clogging and loose joints, restrictions, leaks, and other faulty conditions;

- Provide routine service such as:

- retightening, caulking, lubricating, and performing first echelon maintenance.

The Contractor shall furnish all supplies and equipment needed for the repairs.

C.2.3	ELECTRICAL SERVICES

The Contractor shall perform the following electrical services and use the checklist in Section J, Exhibit 4.

- Evaluate the operating condition and safety of all systems and equipment, including:

- electrical outlets, switches, wiring, installed appliances, doorbells, intercoms, ceiling fans, light fixtures, water heaters, circuit breakers, fuse boxes and feed line connections.

- Make basic repairs, including:

- resetting circuit breakers or replacing fuses, fixing loose connections, replacing switches, etc.

The Contractor will provide all materials.

C.2.4	HVAC SERVICES

General Notes

Task Elements for the Installation of the Split Unit Air conditioners for the residences. The inside unit must be installed above the window level but below the ceiling, in a location to be determined in consultation with the Contracting Officer Representative. The outside condensing unit shall be installed on the walls of the building in a location and in a manner acceptable to the Contracting Officer Representative. The contractor shall work with the contracting Officer’s Representative to determine the exact location where the unit should be installed. The installation process shall be done in a way which will not damage any of the prefab walls .The Contractor shall supply all piping, insulation and flexible electrical cables including an Isolation Switch. Any and all the wall penetrations/caulking shall be completed and repaired in accordance with all applicable building codes, and with the approval of the contracting Officer’s Representative. Any and all floor, wall, and roof penetrations shall be completed and repaired in accordance with all applicable building codes, and with the approval of the Contracting Officer’s Representative. Any and all electrical

wiring and other electrical tasks needed for this project shall be done by a qualified and licensed electrician in accordance with all applicable electrical codes. All other miscellaneous work tasks not mentioned above that is required to install the new AC Units must be performed by the contractor as part of this project. All work areas shall be left clean when work is completed each day. All unused parts, materials, boxes, and other miscellaneous materials used in installing the system shall be removed by the contractor upon completion of the project. All necessary supplies and materials needed to mount and install the Air-conditioning system shall be provided as part of this contract. All equipment and other materials used in this project shall be installed in accordance with equipment manufacturer recommendations and industry best practices. The contractor shall provide qualified personnel at all times while work is in progress. An Air conditioning Technician shall serve as the contractor's project lead, and shall be on-site during the AC system installation

The Contractor shall perform the following HVAC services using the checklist in Section J, Exhibit 4.

- Inspect all HVAC work including:

- pipes, ducts, valves, filters, dampers, fittings, waste water and sewer lines, traps, catch basins, toilet fixtures, down-spouts, and gutters for clogging and loose joints, restrictions, leaks, and other faulty conditions;

- provide routine servicing such as

- retightening, caulking, lubricating, replacing and/or washing filters, and performing first echelon maintenance.

The Contractor shall furnish all supplies and equipment needed for the repairs.

- Inspect pumps for abnormal temperature, vibration, noise, and other trouble symptoms, and adjusting as necessary.

- Inspect valves for restriction, leaks and other trouble symptoms, and adjusting as necessary.

- Inspect cooling towers, checking condition of cooling water, if dirty replacing with clean water.

- Clean strainers when replacing cooling water.  Ensure that the water treatment equipment is properly working and that the water is being treated in accordance with manufacturer's recommendations.

- Perform cleaning, washing and/or replacing of all air filters for indoor units, air handling and fan coil units.  The term "cleaning" means "dusting" where unwashable filters are used, "washing", where washable filters are used. and "replacing" where unwashable/throwaway filters are used.

- Make insulation tests, adjust relays, reset circuit breakers, and clean contact surfaces.

- Carry our full service on the split units as follows:

Clean the air filters by vacuum cleaning and /or washing with detergent and water, air drying thoroughly, and reinstalling. Keep the outdoor coil clean for complete airflow and proper operation. Do not allow leaves, grass clippings, or other material to obstruct the coil.

If the coil becomes obstructed, clean it with water from a garden hose.

a. First turn off electrical power to the outdoor unit.

b. Remove the top with the outdoor fan attached.

c. Flush water through the coil from the inside out.

d. Replace the top and turn on the electrical power.

i. There are commercial coil cleaning solvents. Follow the solvent manufacturer's instructions when using. Normally the solvent is sprayed onto the coil. Allow several minutes for the solvent

C.2.5	CARPENTRY SERVICES

The Contractor shall perform the following carpentry services using the checklist in Section J, Exhibit 4.

- The Contractor shall inspect all:

- wood cabinets, closets, doors, moldings, panels, fixtures, furniture pieces, stairways, including railings, balustrades, treads, risers and nosings, along with all doors in the residence.  Also, inspect all toilet paper holders, soap trays, towel racks, shower curtain rods, toilet seats, medicine cabinets, venetian blind brackets, clothing rails, curtain rods, and any other like items.

- All necessary minor repairs shall be made to all items listed above, 	including:

- repairing, adjusting and/or replacing hinges, latches, closet rods, shelves, moldings and wood panels, cracks and chips, bathroom fixtures, curtain rods and venetian blinds, and caulking and staining repaired areas to match the color of the original wood.

C.2.6	ROOFING SERVICES

The Contractor shall perform the following roofing services using the checklist in Section J, Exhibit 4.

- The Contractor shall inspect:

- the roof and eaves for leaks or other evidence of damage.

- Inspect all rain gutters and water drains for blockages and leaks, and inspect all water catchers for proper positioning.

- The Contractor shall make minor repairs to:

- the roof membrane, including patching leaks, repairing shingles

- rain gutters and drains.

C.2.7	MASONRY SERVICES

The Contractor shall perform the following masonry services using the checklist in Section J, Exhibit 4.

The Contractor shall:

- Inspect all stone and concrete work, including exterior and interior walks, floors, partitions, walls, and stone facing, for breaks, cracks, crumbling and other deterioration.

- make necessary repairs.

C.2.8	GENERAL MECHANICAL SERVICES

The Contractor shall perform the following general mechanical services using the checklist in Section J, Exhibit 4.

The contractor shall:

- Inspect and repair all garage doors, fences, gates, windows, sliding doors, doorstops, and interior fixtures, including door knockers, and pull cords.

- Inspect and clean all vents, including kitchen, bathroom, and dryer vents.

C.2.9	SAFETY EQUIPMENT SERVICES

The Contractor shall perform the following safety Equipment services using the checklist in Section J, Exhibit 4.

The Contractor shall inspect all fire extinguishers and fire extinguishing systems smoke, heat, and carbon monoxide detectors in all areas for proper operation and report the results to the COR.

C.3	MAJOR REPAIRS

The Contractor shall immediately inform the COR or the Embassy Buildings Management Office of major safety problems and the need for major and/or specialized repairs to any part of the serviced area of the residential unit.  The Contractor shall also inform the COR of a major problem in the residential unit in a system or area that is not being serviced as well.  The Contractor shall be liable for the costs for any damage that occurs as a result of the Contractor’s negligence in its duty to inform the COR.  The Contractor shall make efforts to minimize such trouble or damage in systems or areas being serviced until proper corrective action can be taken.

Major and specialized repairs shall be carried out by the Government, independent of this contract.

C.4	CONTRACTOR PERSONNEL

All personnel assigned by the Contractor for the performance of the respective services shall be regular employees of the Contractor, and shall be supervised by the Contractor.  There shall be no employer-employee relationship between the Government and the personnel.  Subcontractors may only be employed with the express written consent of the Contracting Officer.

C.5      SUPERINTENDENCE BY CONTRACTOR

The entire operation of the contracted services shall be superintended by the Contractor's bilingual English liaison.  The liaison shall coordinate the performance of the contracted services with the needs of the Government.

The liaison, or a qualified assistant, shall be on duty throughout the normal operating hours of the Embassy listed in Section F.8.  The liaison shall also superintend the performance of the contracted services on Saturdays, Sundays, and holidays.

C.6       QUALITY ASSURANCE

The Contractor shall institute an appropriate inspection system including:

- Develop and maintain checklists of duties to be carried out,

- Ensure these duties are carried out by the supervisory staff and senior employees, and

- Perform inspections at all work locations to determine whether the various services are being performed according to the contract requirements.

The Contractor shall provide copies of all inspection reports to the COR.

The Contractor shall promptly correct and impove any shortcomings and/or substandard conditions noted in such inspections. The Contractor shall to the attention of the Contracting Officer or COR, for disposition, any conditions beyond the responsibility of the Contractor.

C.7	INSPECTION BY GOVERNMENT

The services performed and the supplies furnished for this contract will be inspected from time to time by the COR, or his/her authorized representatives, to determine that all work is being performed in a satisfactory manner, and that all supplies are of acceptable quality and standards.

The Contractor shall be responsible for any corrective action, within the scope of this contract, which may be required by the Contracting Officer as a result of such inspection.

SECTION D - PACKAGING AND MARKING

D.1	The Contractor shall mark materials delivered to as follows:

Facility Management Office,

U.S. Embassy, Lusaka

Subdivision 694 / Stand 100

Ibex Hill

Lusaka, Zambia.

SECTION E - INSPECTION AND ACCEPTANCE

E.1	52.252-2      CLAUSES INCORPORATED BY REFERENCE (FEB 1998)

This contract incorporates the following clauses by reference, with the same force and effect as if they were given in full text.  Upon request, the Contracting Officer will make their full text available.  Also, the full text of a clause may be accessed electronically at:  http://acquisition.gov/far/index.html or http://farsite.hill.af.mil/vffara.htm.  Please note these addresses are subject to change.

If the Federal Acquisition Regulation (FAR) is not available at the locations indicated above, use the Department of State Acquisition website at http://www.statebuy.state.gov/ to access the links to the FAR.  You may also use an Internet “search engine” (for example, Google, Yahoo or Excite) to obtain the latest location of the most current FAR.

The following Federal Acquisition Regulation clause(s) is/are incorporated by reference:

CLAUSE	TITLE AND DATE

52.246-4	INSPECTION OF SERVICES - FIXED PRICE (AUG 1996)

52.246-12	INSPECTION OF CONSTRUCTION (AUG 1996)

SECTION F - DELIVERIES OR PERFORMANCE

F.1	52.252-2     CLAUSES INCORPORATED BY REFERENCE (FEB 1998)

This contract incorporates the following clauses by reference, with the same force and effect as if they were given in full text.  Upon request, the Contracting Officer will make their full text available.  Also, the full text of a clause may be accessed electronically at:  http://acquisition.gov/far/index.html or http://farsite.hill.af.mil/vffara.htm.  Please note these addresses are subject to change.

If the Federal Acquisition Regulation (FAR) is not available at the locations indicated above, use the Department of State Acquisition website at http://www.statebuy.state.gov/ to access the links to the FAR.  You may also use an Internet “search engine” (for example, Google, Yahoo or Excite) to obtain the latest location of the most current FAR.

The following Federal Acquisition Regulation clause(s) is/are incorporated by reference:

CLAUSE	TITLE AND DATE

52.242-14	SUSPENSION OF WORK (APR 1984)

52.242-15	STOP-WORK ORDER (AUG 1989)

52.242-17	GOVERNMENT DELAY OF WORK (APR 1984)

52.211-12	LIQUIDATED DAMAGES – CONSTRUCTION (SEPT 2000)

(a)	If the Contractor fails to complete the work within the time specified in the contract, or any extension, the Contractor shall pay liquidated damages to the Government in the amount of $200 for each calendar day of delay until the work is completed or accepted.

(b)	If the Government terminates the Contractor’s right to proceed, liquidated damages will continue to accrue until the work is completed.  These liquidated damages are in addition to excess costs of repurchase under the Termination clause.

(End of clause)

F.2	Period of Performance.  The performance period of this contract is from the start date in Notice to Proceed and continuing for 12 months, with four (4), one-year options to renew.  The initial period of performance includes any transition period authorized under the contract.

F.3.	DELIVERABLES

The Contractor shall deliver the following items:

| Description | Quantity | Delivery Date | Deliver To: |
| --- | --- | --- | --- |
| H.12.2 – Biographies of Personnel | 1 | 10 days after award | COR |
| H.3 – Bonds | 1 | 30 days after award | CO |
| H.4 – Insurance/Licenses & Permits | 1 | 30 days after award | CO |
| H.10.1 – Safety Plan | 1 | 30 days after award | COR |
| H.7.1 – Waste Disposal Report | 1 | Last day of each month | COR |

F.4	CONTRACTOR'S SUBMISSION OF WORK SCHEDULE FOR TASK ORDERS FOR MAJOR REPAIRS

The time for submission of the schedules and General Instructions referenced in Section I, 52.236-15, "Schedules for Construction Contracts,” Paragraph (a) is modified to reflect the due date for submission as 5 calendar days after receipt of an executed contract."  The Contractor shall revise such schedules weekly:

(a)  to account for the actual progress of the work,

(b)  to reflect approved adjustments in the performance schedule, and

(c)  as required by the Contracting Officer to achieve coordination with work by the Government and any separate contractors employed by the Government.

The Contractor shall submit a schedule that sequences work to minimize disruption at the job site.

All deliverables shall be in the English language and any system of dimensions (such as English or metric) shown shall be consistent with the contract.  If the Contractor has failed to act promptly and responsively in submitting its deliverables, the Government in approving such deliverables shall allow no extension of time for delay.  The Contractor shall identify each deliverable as required by the contract.

F.5	ACCEPTANCE OF SCHEDULE

When the Government has accepted any time schedule, it shall be binding on the Contractor.  The completion date is fixed and may be extended only by a written modification to the task order signed by the Contracting Officer.  Acceptance or approval of any schedule or revision thereof by the Government shall not:

- extend the completion date or obligate the Government to do so,

- constitute acceptance or approval of any delay, nor

- excuse the Contractor from or relieve the Contractor of its obligation to maintain the progress of the work and achieve final completion by the established completion date.

F.6	NOTICE OF DELAY

The Contractor shall notify the Government if the contractor receives a notice of any change in the work, or if any other conditions arise that may cause or are actually causing delays and the Contractor believes may result in completion of the project after the completion date.  The notification shall state the effect, if any, of such change or other conditions upon the approved schedule, and shall state in what respects, if any, the relevant schedule or the completion date should be revised.  The Contractor shall give such notice promptly, not more than ten (10) days following the first occurrence of event giving rise to the delay or prospective delay.  The Contractor shall obtain the approval of the Contracting Officer for any revisions to the approved time schedule.

F.7	NOTICE TO PROCEED

(a)  Following receipt from the Contractor of acceptable bonds or evidence of insurance within the time specified in Section H of this contract, the Contracting Officer will provide to the Contractor a Notice to Proceed.  The Contractor shall then begin work.

(b)  It is possible that the Contracting Officer may elect to issue the Notice to Proceed before receipt and acceptance of any bonds or evidence of insurance.  Issuance of a Notice to Proceed by the Government before receipt of the required bonds or insurance certificates or policies shall not be a waiver of the requirement to furnish these documents.

# F.8	WORKING HOURS

The Contractor shall perform all work during working hours from 08:00am to 17:00pm Monday through Friday except for the holidays identified in Sections I.15.  The Contracting Officer may approve other hours.  The Contractor shall give 24 hours advance notice to the Contracting Officer, who may consider any deviation from the hours identified above.  Changes in work hours will not be a cause for a price increase if initiated by the Contractor.

F.9	EXCUSABLE DELAYS

The Contractor will be allowed time, not money, for excusable delays as defined in FAR 52.249-10, Default.  Examples of such cases include:

(l)	acts of God or of the public enemy,

(2)	acts of the United States Government in either its sovereign or contractual 			capacity,

(3)	acts of the government of the host country in its sovereign capacity,

(4)	acts of another contractor in the performance of a contract with the 				Government,

(5)	fires,

(6)	floods,

(7)	epidemics,

(8)	quarantine restrictions,

(9)	strikes,

(l0)	freight embargoes,

(11)	delays in delivery of Government furnished equipment and

(12)	unusually severe weather.

In each instance, the failure to perform must be beyond the control and without the fault or negligence of the Contractor, and the failure to perform furthermore

- must be one that the Contractor could not have reasonably anticipated and taken adequate measures to protect against,

- cannot be overcome by reasonable efforts to reschedule the work, and

- directly and materially affects the date of final completion of the project.

F.10	POST AWARD CONFERENCE

The Government will hold a post award conference ten (10) days after contract award at U.S Embassy Lusaka, Subdivision 694/Stand 100 Ibex Hill Road, Lusaka, Zambia to discuss the location and type of residences to be serviced, submittals, personnel issues, procedures and other important matters concerning the contract.

SECTION G - CONTRACT ADMINISTRATION DATA

G.1 	652.242-70    CONTRACTING OFFICER'S REPRESENTATIVE (COR) (AUG 1999)

(a)	The Contracting Officer may designate in writing one or more Government employees, by name or position title, to take action for the Contracting Officer under this contract.  Each designee shall be identified as a Contracting Officer’s Representative (COR).  Such designation(s) shall specify the scope and limitations of the authority so delegated; provided, that the designee shall not change the terms or conditions of the contract, unless the COR is a warranted Contracting Officer and this authority is delegated in the designation.

(b)	The COR for this contract is Project Coordinator.

# G.1.2  Duties

The COR is responsible for inspection and acceptance of services. These duties include review of contractor invoices, including the supporting documentation required by the contract. The COR may provide technical advice, substantive guidance, inspections, invoice approval, and other purposes as deemed necessary under the contract.

G.2	PAYMENT

The Financial Management Office

US Embassy Lusaka

Plot 694 / Lot 100

Kabulonga Road, Ibex Hill

Lusaka, Zambia.

Post Code: 10101

Email: Lusakainvoices@state.gov

G.2.1	GENERAL

The Contractor shall follow Section I, 52.232-5, "Payments Under Fixed-Price Construction Contracts.”  The following subsections elaborate upon the information contained in that clause.

G.2.2	DETAIL OF PAYMENT REQUESTS

The Contractor’s requests for payment, which shall be made no more frequently than monthly shall cover the value of labor and materials completed and in place, including a prorated portion of overhead and profit.

G.2.3	PAYMENTS TO SUBCONTRACTORS

The Contractor shall make timely payment from the proceeds of the progress or final payment to subcontractors and suppliers following the Contractor's contractual arrangements with them.

G.2.4	EVALUATION BY THE CONTRACTING OFFICER

The Contracting Officer shall make a determination as to the amount that is due after an inspection of the work.  The Contracting Officer shall advise the Contractor if the Contracting Officer does not approve payment of the full amount applied for, less the retainage addressed in FAR 52.232-5.

G.2.5	ADDITIONAL WITHHOLDING

Independently of monies retained by the Government under FAR 52.232-5 the Government may withhold from payments due the Contractor any amounts necessary to cover:

- Wages or other amounts due the Contractor's employees on this project;

- Wages or other amounts due employees of subcontractors on this project;

(c)  Amounts due suppliers of materials or equipment for this project; and

(d)  Any other amounts that the Contractor may be held liable under this contract, including but not limited to the actual or prospective costs of correction of defective work and costs for failure to make adequate progress.

G.2.6.	PAYMENT

In accordance with 52.232-27(a), the 14-day period identified in FAR 52.232-27(a)(1)(i)(A) is changed to 30 days.

G.3	RECORDKEEPING REQUIREMENTS

The Contractor and the COR shall both maintain a complete and accurate management file.  The file shall contain, as a minimum, the following items:

(a)  The Government's copies of all task orders issued under this contract, and all inspection reports completed by the COR (OF-127).  These forms will be supplied to advise the Contractor of service requests and to document the performance of all work.

(b)  Contractor’s Service Report forms, documenting arrival and departure time of the contractor's representative performing the service, and all information on parts installed for major repairs only.

(c)	Documentation of any complaints from post personnel or unusual incidents that may have taken place during the visit to the site.

SECTION H - SPECIAL CONTRACT REQUIREMENTS

H.1	ISSUANCE OF ORAL TASK ORDERS

The Contracting Officer may issue oral task orders, as stated in Section B.4.1.  Any oral task orders issued shall be confirmed in writing within three days when the Mission is open for business.  U.S. or local holidays observed by the Mission and natural disasters or other emergencies that result in a suspension of normal operations shall not be counted against the three-day period.  In all cases, the Contractor must begin work after receipt of an oral order, without waiting for written confirmation.

H.2	ORDERING OFFICIAL

The designated ordering individual for this contract is the Contracting Officer.

H.3	BOND REQUIREMENTS

H.3.1	TYPE OF BONDS

### The Contractor shall furnish:

(1) a performance and guaranty bond and a payment bond on forms provided by and from sureties acceptable to the Government, each in the amount of 20% of the maximum amount of services per contract term (see B.2); or

(2)  comparable alternate performance security approved by the Government such as a letter of credit shown in Section J.

H.3.2	TIME FOR SUBMISSION

The Contractor shall provide the bonds required by Paragraph H.1.1 within ten (10) days after contract award.  Failure to submit:

(1)  the required bonds other security acceptable to the Government;

(2)  bonds from an acceptable surety; or

(3)  bonds in the required amount,

may result in rescinding or termination of the contract by the Government.

The Contractor shall be liable for costs described in FAR 52.249-10, "Default (Fixed-Price Construction) if the contract is terminated.

H.3.3	COVERAGE

The bonds or alternate performance security shall guarantee:

(a)  the Contractor's completion of the work within the contract time,

(b)  the correction of any defects after completion as required by this 			contract,

- the payment of all wages and other amounts payable by the Contractor 			under its subcontracts or for labor and materials, and

- the satisfaction or removal of any liens or encumbrances placed on the 			work.

H.3.4	DURATION OF COVERAGE

The required performance and payment securities shall remain in effect in the full amount required until final acceptance of the project by the Government.  At that time, the penal sum of the performance security only shall be reduced to 10% of the contract price.  The performance security shall remain in effect for one year after the date of final completion and acceptance, and the Contractor shall pay any premium required for the entire period of coverage.  The requirement for payment security terminates at final acceptance.

H.3.5	52.228-2   ADDITIONAL BOND SECURITY (OCT 1997)

The Contractor shall promptly furnish additional security required to protect the Government and persons supplying labor or materials under this contract if –

- Any surety upon any bond, or issuing financial institution for other security, furnished with this contract becomes unacceptable to the Government;

- Any surety fails to furnish reports on its financial condition as required by the Government; or

(c)  The contract price is increased so that the penal sum of any bond becomes inadequate in the opinion of the Contracting Officer; or

(d)  An irrevocable letter of credit (ILC) used as security will expire before the end of the period of required security.  If the Contractor does not furnish an acceptable extension or replacement ILC, or other acceptable substitute, at least 30 days before an ILC’s scheduled expiration, the Contracting Officer has the right to immediately draw on the ILC.

H.4	INSURANCE

H.4.1	AMOUNT OF INSURANCE

The Contractor is required to provide whatever insurance is legally necessary under Section I, 52.228-5, "Insurance - Work on a Government Installation.”  The Contractor shall, at its own expense, provide and maintain during the entire performance period the following insurance amounts:

General Liability (includes premises/operations, collapse hazard, products, completed operations, contractual, independent contractors, broad form property damage, personal injury)

| General Liability |
| --- |
| (1) Bodily injury on or off the site in U.S. dollars: |
| Per Occurrence | $10,000.00 |
| Cumulative | $50,000.00 |
| (2) Property damage on or off the site in U.S. dollars: |
| Per Occurrence | $10,000.00 |
| Cumulative | $50,000.00 |

The types and amounts of insurance are the minimums required.  The Contractor shall obtain any other types of insurance required by local law or that are ordinarily or customarily obtained in the location of the work.  The limit of such insurance shall be as provided by law or sufficient to meet normal and customary claims.

The Contractor agrees that the Government shall not be responsible for personal injuries or for damages to:

- any property of the Contractor,

- its officers,

- agents,

- servants,

- employees, or

- any other person,

arising from and incident to the Contractor's performance of this contract.

The Contractor shall hold harmless and indemnify the Government from any and all claims arising, except in the instance of gross negligence on the part of the Government.

The Contractor shall obtain adequate insurance for damage to, or theft of, materials and equipment in insurance coverage for loose transit to the site or in storage on or off the site.

The Contractor shall provide Defense Base Act (DBA) insurance covering their employees working on the contract to include American citizens, Individuals hired in the United States or its possessions, regardless of citizenship, Host Country Nationals (HCNs) and Third Country Nationals (TCNs) working outside of the United States.  The Contractor shall obtain DBA insurance directly from any Department of Labor approved providers at the DOL website at http://www.dol.gov/owcp/dlhwc/lscarrier.htm

H.4.2	GOVERNMENT AS ADDITIONAL INSURED

The general liability policy required of the Contractor shall name "the United States of America, acting by and through the Department of State,” as an additional insured with respect to operations performed under this contract.

H.4.3	TIME FOR SUBMISSION OF EVIDENCE OF INSURANCE

The Contractor shall provide evidence of the insurance within ten (10) days after contract award.  Failure to timely submit this evidence, in a form acceptable to the Contracting Officer, may result in rescinding or termination of the contract by the Government.

H.5	GOVERNING LAW

The laws of the United States shall govern the contract and the interpretation of the contract.

H.6	LANGUAGE PROFICIENCY

The manager, assigned by the Contractor to superintend the work on-site required by 52.236-6, "Superintendence by the Contractor” shall be fluent in written and spoken English.

H.7	LAWS AND REGULATIONS

H.7.1	COMPLIANCE REQUIRED

The Contractor shall, without additional expense to the Government, be responsible for complying with all host country laws, codes, ordinances, and regulations applicable to the performance of the work, and with the lawful orders of any governmental authority having jurisdiction.  Host country authorities may not enter the construction site without the permission of the Contracting Officer.  Unless directed by the Contracting Officer, the Contractor shall comply with the more stringent of:

(a)  the requirements of such laws, regulations and orders; or

(b)  the contract.

If a conflict between the contract and such laws, regulations and orders, the Contractor shall promptly advise the Contracting Officer of the conflict and recommend a proposed course of action for resolution by the Contracting Officer.

H.7.2	LABOR, HEALTH AND SAFETY LAWS AND CUSTOMS

The Contractor shall comply with all local labor laws, regulations, customs and practices pertaining to labor, safety, and similar matters, unless doing so would be inconsistent with the requirements of this contract.

H.7.3	SUBCONTRACTORS

The Contractor shall give written assurance to the Contracting Officer that all subcontractors and others performing work on or for the project have obtained all required licenses and permits.

H.7.4	EVIDENCE OF COMPLIANCE

The Contractor shall submit proper documentation and evidence of compliance with this clause to the Contracting Officer.

H.8	RESPONSIBILITY OF CONTRACTOR

H.8.1	DAMAGE TO PERSONS OR PROPERTY

The Contractor shall be responsible for all damages to persons or property that occur as a result of the Contractor's fault or negligence.  The Contractor shall take proper safety and health precautions to protect the work, the workers, the public, and the property of others.

H.8.2	RESPONSIBILITY FOR WORK PERFORMED

The Contractor shall be responsible for all materials delivered and work performed until final completion and acceptance of the entire work, except for any completed unit of work that may have been accepted in writing under the contract.

H.9	MAINTENANCE OPERATIONS

H.9.1	OPERATIONS AND STORAGE AREAS

(a)  Confinement to Authorized Areas.  The Contractor shall confine all operations (including storage of materials) on Government premises to areas authorized or approved by the Contracting Officer.

(b)  Vehicular Access.  The Contractor shall use only established site entrances and roadways.

H.9.2	USE OF PREMISES

(a)  Occupied Premises.  If the premises are occupied, the Contractor, its subcontractors, and their employees shall comply with the regulations promulgated by the Government governing access to, operation of, and conduct while in or on the premises.  The Contractor shall perform the work required under this contract without unreasonably interrupting or interfering with the conduct of Government business.

(b)  Requests from Occupants.  The Contractor shall refer to the Contracting Officer any request received by the Contractor from occupants of existing buildings to change the sequence of work.

- Access Limited.  The Contractor, its subcontractors and their employees shall not have access to or be admitted into any building or portion of the site outside the areas designated in this contract except with the permission of the Contracting Officer.

H.10	SAFETY

H.10.1	  652.236-70	ADDITIONAL SAFETY MEASURES (OCT 2017)

In addition to the safety/accident prevention requirements of FAR 52.236-13, Accident Prevention Alternate I, the contractor shall comply with the following additional safety measures.

(a)  High Risk Activities.  If the project contains any of the following high risk activities, the contractor shall follow the section in the latest edition, as of the date of the solicitation, of the U.S. Army Corps of Engineers Safety and Health manual, EM 385-1-1, that corresponds to the high risk activity.  Before work may proceed, the contractor must obtain approval from the COR of the written safety plan required by FAR 52.236-13, Accident Prevention Alternate I (see paragraph (f) below), containing specific hazard mitigation and control techniques.

(1) Scaffolding;

(2) Work at heights above 1.8 meters;

(3) Trenching or other excavation greater than one (1) meter in depth;

(4) Earth-moving equipment and other large vehicles;

(5) Cranes and rigging;

(6) Welding or cutting and other hot work;

(7) Partial or total demolition of a structure;

(8) Temporary wiring, use of portable electric tools, or other recognized electrical hazards.  Temporary wiring and portable electric tools require the use of a ground fault circuit interrupter (GFCI) in the affected circuits; other electrical hazards may also require the use of a GFCI;

(9) Work in confined spaces (limited exits, potential for oxygen less than 19.5 percent or combustible atmosphere, potential for solid or liquid engulfment, or other hazards considered to be immediately dangerous to life or health such as water tanks, transformer vaults, sewers, cisterns, etc.);

(10) Hazardous materials - a material with a physical or health hazard including but not limited to, flammable, explosive, corrosive, toxic, reactive or unstable, or any operations, which creates any kind of contamination inside an occupied building such as dust from demolition activities, paints, solvents, etc.; or

(11) Hazardous noise levels as required in EM 385-1 Section 5B or local standards if more restrictive.

(b)  Safety and Health Requirements.  The contractor and all subcontractors shall comply with the latest edition of the U.S. Army Corps of Engineers Safety and Health manual EM 385-1-1, or OSHA 29 CFR parts 1910 or 1926 if no EM 385-1-1 requirements are applicable, and the accepted contractor’s written safety program.

(c) Mishap Reporting.  The contractor is required to report immediately all mishaps to the COR and the contracting officer.  A “mishap” is any event causing injury, disease or illness, death, material loss or property damage, or incident causing environmental contamination.  The mishap reporting requirement shall include fires, explosions, hazardous materials contamination, and other similar incidents that may threaten people, property, and equipment.

(d) Records.  The contractor shall maintain an accurate record on all mishaps incident to work performed under this contract resulting in death, traumatic injury, occupational disease, or damage to or theft of property, materials, supplies, or equipment.  The contractor shall report this data in the manner prescribed by the contracting officer.

(e) Subcontracts.  The contractor shall insert this clause, including this paragraph (e), with appropriate changes in the designation of the parties, in subcontracts.

(f) Written program.  The plan required by paragraph (f)(1) of the clause entitled “Accident Prevention Alternate I” shall be known as the Site Safety and Health Plan (SSHP) and shall address any activities listed in paragraph (a) of this clause, or as otherwise required by the contracting officer/COR.

- The SSHP shall be submitted at least 10 working days prior to commencing any activity at the site.

- The plan must address developing activity hazard analyses (AHAs) for specific tasks.  The AHAs shall define the activities being performed and identify the work sequences, the specific anticipated hazards, site conditions, equipment, materials, and the control measures to be implemented to eliminate or reduce each hazard to an acceptable level of risk.  Work shall not begin until the AHA for the work activity has been accepted by the COR and discussed with all engaged in the activity, including the Contractor, subcontractor(s), and Government on-site representatives.

(3)  The names of the Competent/Qualified Person(s) required for a particular activity (for example, excavations, scaffolding, fall protection, other activities as specified by EM 385-1-1) shall be identified and included in the AHA.  Proof of their competency/qualification shall be submitted to the contracting officer or COR for acceptance prior to the start of that work activity.  The AHA shall be reviewed and modified as necessary to address changing site conditions, operations, or change of competent/qualified person(s).

(End of clause)

H.11	SUBCONTRACTORS AND SUPPLIERS

H.11.1  CLAIMS AND ENCUMBRANCES

The Contractor shall satisfy all lawful claims of any persons or entities employed by the Contractor, including:

(a)  subcontractors,

(b)  material men and laborers,

for all labor performed and materials furnished under this contract, including the applicable warranty or correction period.

The Contractor shall not at any time permit any lien, attachment, or other encumbrance to be entered against or to remain on the building(s) or the premises as a result of nonperformance of any part of this contract.

H.11.2	 APPROVAL OF SUBCONTRACTORS

(a)  Review and Approval.  The Government reserves the right to review proposed subcontractors for a period of five (5) days before providing notice of approval or rejection.

(b)  Rejection of Subcontractors.  The Government reserves the right to reject any or all subcontractors proposed if their participation in the project may cause damage to the national security interests of the United States.  The Contractor agrees to promptly replace any subcontractor rejected by the Government under this clause.

H.12	CONTRACTER PERSONNEL

H.12.1	 REMOVAL OF PERSONNEL

The Contractor shall:

(a)  maintain discipline at the site and at all times;

(b)  take all reasonable precautions to prevent any unlawful, riotous or disorderly conduct by or amongst those employed at the site; and

(c)  take all reasonable precautions for the preservation of peace and protection of persons and property in the neighborhood of the project against unlawful, riotous, or disorderly conduct.

The Contracting Officer may require, in writing, that the Contractor remove from the work any employee that the Contracting Officer determines:

(a)  incompetent,

(b)  careless,

(c)  insubordinate or

(d)  otherwise objectionable, or

(e)  whose continued employment on the project is deemed by the Contracting Officer to be contrary to the Government's interests.

H.12.2	  MAINTENANCE PERSONNEL SECURITY

After award of the contract, the Contractor  has ten (10) calendar days to submit to the Contracting Officer  a list of workers and supervisors assigned to this project for the Government to conduct security checks.  It is anticipated that security checks will take 5 days to perform.  For each individual the list shall include:

- Full Name

- Place and Date of Birth

- Current Address

- Identification number

- Motor Vehicle Details

- Equipment used on site.

Failure to provide any of the above information may be considered grounds for rejection and/or re-submittal of the application.  Once the Government has completed the security screening and approved the applicants a badge will be provided to the individual for access to the site.  The Government may revoke this badge at any time due to the falsification of data, or misconduct on site.

H.13	MATERIALS AND EQUIPMENT

H.13.1	  SELECTION AND APPROVAL OF MATERIALS

(a)  Standard of Quality.  All materials and equipment incorporated into the work shall be new and for the purpose intended, unless otherwise specified.  All workmanship shall be of good quality and performed in a skillful manner as determined by the Contracting Officer.

(b)  Selection by Contractor.  Where the contract permits the Contractor to select products, materials or equipment to be incorporated into the work, or where specific approval is otherwise required by the contract, the Contractor shall give the Contracting Officer, for approval:

(1)  The names of the manufacturer;

(2)  Model number;

(3)  Source of procurement of each such product, material or equipment; and

(4)  Other pertinent information concerning the:

(i)	 Nature,

(ii)  Appearance,

(iii)  Dimensions,

(iv)  Performance,

(v)   Capacity, and

(vi)  Rating

unless otherwise required by the Contracting Officer.

The Contractor shall provide this information in a timely manner to permit the Government to evaluate the information against the requirements of the contract.  The Contractor shall provide a submittal register ten (10) days after contract award showing when shop drawings, samples, or submittals shall be made.  The Contractor shall submit samples for approval at the contractor's expense, with all shipping charges prepaid, when directed to do so by the Contracting Officer or COR.  Installation or use of any products, materials or equipment without the required approval shall be at the risk of rejection.

H.13.2 	CUSTODY OF MATERIALS

The Contractor shall be responsible for the custody of all materials received for incorporation into the project, including Government furnished materials, upon delivery to the Contractor or to any person for whom it is responsible, including subcontractors.  The Contractor shall deliver all items to the site as soon as practicable.  The Contractor shall clearly mark in a manner directed by the Contracting Officer all items of which the Contractor has custody but that have not been delivered or secured at the site.  The Contractor shall clearly indicate the use of such items for this U.S. Government project.

H.14	SURPLUS MATERIALS

Any surplus materials, fixtures, articles or equipment remaining at the completion of the project shall become the property of the Contractor, except those items furnished by the Government, whose cost is not included in the contract price.

H.15	SPECIAL WARRANTIES

H.15.1 	SPECIAL WARRANTY OBLIGATIONS

Any special warranties that may be required under the contract shall be subject to the terms of FAR 52.246-21, "Warranty of Construction," unless they conflict with the terms of such special warranties.

H.15.2	 WARRANTY INFORMATION

The Contractor shall obtain and furnish to the Government all information that is required to make any subcontractor's, manufacturers, or supplier's guarantee or warranty legally binding and effective.  The Contractor shall submit both the information and the guarantee or warranty to the Government in sufficient time to permit the Government to meet any time limit specified in the guarantee or warranty, but not later than completion and acceptance of all work under this contract.

H.16	NONCOMPLIANCE WITH CONTRACT REQUIREMENTS

The Contracting Officer shall have the right to order the Contractor to suspend any or all work under the contract until the Contractor has complied or begun complying with the noncompliance notice in a reasonable period of time.  The Contractor will not be entitled to any extension of contract time or payment for any costs incurred as a result of being ordered to suspend work for such a cause.  See FAR 52.242-14, Suspension of Work.

SECTION I - CONTRACT CLAUSES

I.1	52.252-2     CLAUSES INCORPORATED BY REFERENCE (FEB 1998)

This contract incorporates the following clauses by reference, with the same force and effect as if they were given in full text.  Upon request, the Contracting Officer will make their full text available.  Also, the full text of a clause may be accessed electronically at:  http://acquisition.gov/far/index.html or http://farsite.hill.af.mil/vffara.htm.  Please note these addresses are subject to change.

If the Federal Acquisition Regulation (FAR) is not available at the locations indicated above, use the Department of State Acquisition website at https://www.ecfr.gov/cgi-bin/text-idx?SID=2e978208d0d2aa44fb9502725ecac4e5&mc=true&tpl=/ecfrbrowse/Title48/48chapter6.tpl to access the links to the FAR.  You may also use an Internet “search engine” (for example, Google, Yahoo or Excite) to obtain the latest location of the most current FAR.

The following Federal Acquisition Regulation clauses are incorporated by reference:

CLAUSE	TITLE AND DATE

52.202-1	DEFINITIONS (NOV 2013)

52.203-3	GRATUITIES (APR 1984)

52.203-5	COVENANT AGAINST CONTINGENT FEES (MAY 2014)

52.203-6	RESTRICTIONS ON SUBCONTRACTOR SALES TO THE 				GOVERNMENT (SEPT 2006)

52.203-7	ANTI-KICKBACK PROCEDURES (MAY 2014)

52.203-8	CANCELLATION, RESCISSION, AND RECOVERY OF FUNDS FOR 			ILLEGAL OR IMPROPER ACTIVITY (MAY 2014)

52.203-10 	PRICE OR FEE ADJUSTMENT FOR ILLEGAL OR IMPROPER 			ACTIVITY (MAY 2014)

52.203-12	LIMITATION ON PAYMENTS TO INFLUENCE CERTAIN FEDERAL 		TRANSACTIONS (OCT 2010)

52.203-17	CONTRACTOR EMPLOYEE WHISTLEBLOWER RIGHTS AND 			REQUIREMENT TO INFORM EMPLOYEES OF WHISTLEBLOWER 			RIGHTS (APR 2014)

52.203-19	PROHIBITON ON REQUIRING CERTAIN INTERNAL CONFIDENTIALITY AGREEMENTS OR STATEMENTS (JAN 2017)

52.204-4	PRINTED OR COPIED DOUBLE-SIDED ON POSTCONSUMER 			FIBER CONTENT PAPER (MAY 2011)

52.204-9 	PERSONAL IDENTITY VERIFICATION OF CONTRACTOR 				PERSONNEL (JAN 2011)

52.204-10	REPORTING EXECUTIVE COMPENSATION AND FIRST-TIER SUBCONTRACT AWARDS	 (OCT 2015)

52.204-18	COMMERCIAL AND GOVERNMENT ENTITY CODE 					MAINTENANCE (JUL 2016)

### 52.204-19	INCORPORATION BY REFERENCE OF REPRESENTATIONS AND 			CERTIFICATIONS (DEC 2014)

### 52.204-23 	PROHIBITION ON CONTRACTING FOR HARDWARE, SOFTWARE, AND SERVICES DEVELOPED OR PROVIDED BY KASPERSKY LAB AND OTHER COVERED ENTITIES (JUL 2018)

52.209-6 	PROTECTING THE GOVERNMENT'S INTEREST WHEN 				SUBCONTRACTING WITH CONTRACTORS DEBARRED, 				SUSPENDED OR PROPOSED FOR DEBARMENT (OCT 2015)

52.209-9          UPDATES OF PUBLICLY AVAILABLE INFORMATION 				REGARDING RESPONSIBILITY MATTERS (JULY 2013)

52.215-2	AUDIT AND RECORDS – NEGOTIATION (OCT 2010)

52.215-8	ORDER OF PRECEDENCE 	- UNIFORM CONTRACT FORMAT			(OCT 1997)

52.215-11	PRICE REDUCTION FOR DEFECTIVE CERTIFIED COST OR 				PRICING DATA – MODIFICATIONS (AUG 2011)

52.215-13	SUBCONTRACTOR CERTIFIED COST OR PRICING DATA – 				MODIFICATIONS (OCT 2010)

52.215-21	REQUIREMENTS FOR CERTIFIED COST OR PRICING DATA

AND DATA OTHER THAN CERTIFIED COST OR PRICING DATA-			MODIFICATIONS (OCT 2010)

52.216-7	ALLOWABLE COST AND PAYMENT (JUN 2013) Alternate I (FEB 1997)

52.222-1	NOTICE TO THE GOVERNMENT OF LABOR DISPUTES (FEB 1997)

52.222-19	CHILD LABOR – COOPERATION WITH AUTHORITIES AND REMEDIES (JAN 2018)

52.222-50 	COMBATING TRAFFICKING IN PERSONS (MAR 2015)

52.223-18	ENCOURAGING CONTRACTOR POLICIES TO BAN TEXT 				MESSAGING WHILE DRIVING (AUG 2011)

52.225-5 	TRADE AGREEMENTS (FEB 2016)

52.225-13	RESTRICTIONS ON CERTAIN FOREIGN	PURCHASES (JUN 2008)

52.225-14	INCONSISTENCY BETWEEN ENGLISH VERSION AND 				TRANSLATION OF CONTRACT (FEB 2000)

52.228-3	Workers’ Compensation Insurance (Defense Base Act) 	(JUL 2014)

52.228-5	INSURANCE-WORK ON A GOVERNMENT INSTALLATION 				(JAN 1997)

52.228-11	PLEDGES OF ASSETS (JAN 2012)

52.228-13	Alternative Payment Protection (JULY 2000)

52.228-14	IRREVOCABLE LETTERS OF CREDIT (NOV 2014)

52.229-6	TAXES - FOREIGN FIXED-PRICE	CONTRACTS	(FEB 2013)

52.232-1	PAYMENTS (	APR 1984)

52.232-5	PAYMENTS UNDER FIXED-PRICE CONSTRUCTION 					CONTRACTS (MAY 2014)

52.232-8	DISCOUNTS FOR PROMPT PAYMENT (FEB 2002)

52.232-17	INTEREST (MAY 2014)

52.232-18	AVAILABILITY OF FUNDS (APR 1984)

52.232-25	PROMPT PAYMENT (JAN 2017)

52.232-27	PROMPT PAYMENT FOR CONSTRUCTION CONTRACT (MAY 			2014)

52.232-32	PERFORMANCE BASED PAYMENTS (APR 2012)

52.232-33	PAYMENT BY ELECTRONIC FUNDS TRANSFER – SYSTEM FOR 			AWARD MANAGEMENT (JULY 2013)

### 52.232-40	Providing Accelerated Payments to Small Business 			Subcontractors (Dec 2013)

52.233-1	DISPUTES (MAY 2014) Alternate I (DEC 1991)

52.233-3	PROTEST AFTER AWARD	(AUG 1996)

52.233-4	APPLICABLE LAW FOR BREACH OF CONTRACT CLAIM

(OCT 2004)

52.236-2	DIFFERING SITE CONDITIONS (APR 1984)

52.236-3	SITE INVESTIGATIONS AND CONDITIONS AFFECTING THE 			WORK (APR 1984)

52.236-5	MATERIAL AND WORKMANSHIP (APR 1984)

52.236-6	SUPERINTENDENCE BY THE CONTRACTOR (APR 1984)

52.236-7	PERMITS AND RESPONSIBILITIES (NOV 1991)

52.236-8	OTHER CONTRACTS (APR 1984)

52.236-9	PROTECTION OF EXISTING VEGETATION, STRUCTURES 				EQUIPMENT, UTILITIES, AND IMPROVEMENTS (APR 1984)

52.236-10	OPERATIONS AND STORAGE (APR 1984)

52.236-11	USE AND POSSESSION PRIOR TO COMPLETION (APR 1984)

52.236-12	CLEANING UP (APR 1984)

52.236-13	ACCIDENT PREVENTION (NOV 1991)

52.236-14	AVAILABILITY AND USE OF UTILITY SERVICES (APR 1984)

52.236-15	SCHEDULES FOR CONSTRUCTION CONTRACTS (APR 1984)

52.236-21	SPECIFICATIONS AND DRAWINGS FOR CONSTRUCTION

(FEB 1997)

52.237-3	CONTINUITY OF SERVICES (JAN 1991)

52.242-13	BANKRUPTCY (JULY 1995)

52.243-1	CHANGES - FIXED-PRICE (AUG 1987) Alternate II (APR 1984)

52.244-06  	SUBCONTRACTS FOR COMMERCIAL ITEMS (AUG 2018)

52.245-1	GOVERNMENT PROPERTY (JAN 2017)

52.245-2	GOVERNMENT PROPERTY INSTALLATION OPERATION SERVICES (APR 2012)

52.246-21	WARRANTY OF CONSTRUCTION (MAR 1994)

52.248-1	VALUE ENGINEERING (OCT 2010)

52.249-4	TERMINATION FOR CONVENIENCE OF THE GOVERNMENT 			(SERVICES) (SHORT FORM) (APR 1984)

52.249-8	DEFAULT (FIXED-PRICE SUPPLY AND SERVICE) (APR 1984)

52.249-14	EXCUSABLE DELAYS (APR 1984)

52.253-1	COMPUTER GENERATED FORMS (JAN 1991)

I.2.	Federal Acquisition Regulation Clauses Provided in Full 	Text

The following FAR clauses are provided in full text:

52.203-08	CANCELLATION, RESCISSION AND RECOVERY OF FUNDS FOR 			ILLEGAL OR IMPROPER ACTIVITY (JAN 1997)

(a)  If the Government receives information that a contractor or a person has engaged in conduct constituting a violation of subsection (a), (b), (c), or (d) of Section 27 of the Office of Federal Procurement Policy Act (41 U.S.C. 423 (The Act)), as amended by section 4304 of the 1996 National Defense Authorization Act for Fiscal Year 1996 (Public Law 104-106), the Government may-

(1)	Cancel the solicitation, if the contract has not yet been awarded or 			issued; or

(2)	Rescind the contract with respect to which-

(i)	The Contractor or someone acting for the Contractor has been convicted for an offense where the conduct constitutes a violation of subsection 27(a) or (b) of the Act for the purpose of either-

- Exchanging the information covered by such subsections for anything of value; or

- Obtaining or giving anyone a competitive advantage in the award of a Federal agency procurement contract; or

(ii)	The head of the contracting activity has determined, based upon a preponderance of the evidence, that the Contractor or someone acting for the Contractor has engaged in conduct constituting an offense punishable under subsections 27(e)(1) of the Act.

(b)  If the Government rescinds the contract under paragraph (a) of this clause, the Government is entitled to recover, in addition to any penalty prescribed by law, the amount expended under the contract.

(c)  The rights and remedies of the Government specified herein are not exclusive, and are in addition to any other rights and remedies provided by law, regulation, or under this contract.

(End of clause)

I.3	52.216-18   ORDERING (OCT 1995)

(a)  Any supplies and services to be furnished under this contract shall be ordered by issuance of delivery orders or task orders by the individuals or activities designated in the Schedule.  Such orders may be issued from date of award through base period or option periods if exercised.

(b)  All delivery orders or task orders are subject to the terms and conditions of this contract.  In the event of conflict between a delivery order or task order and this contract, the contract shall control.

(c)  If mailed, a delivery order or task order is considered "issued" when the Government deposits the order in the mail.  Orders may be issued orally, by facsimile, or by electronic commerce methods only if authorized in the Schedule.

(End of clause)

I.4	52.216-19   ORDER LIMITATIONS (OCT 1995)

(a)  Minimum Order.  When the Government requires supplies or services covered by this contract in an amount of less than $100.00, the Government is not obligated to purchase, nor is the Contractor obligated to furnish, those supplies or services under the contract.

(b)  Maximum Order.  The Contractor is not obligated to honor--

- Any order for a single item in excess of $150,000.00;

- Any order for a combination of items in excess of $150,000.00; or

- A series of orders from the same ordering office within 5 days that together call for quantities exceeding the limitation in subparagraph (1) or (2) above.

(c)  If this is a requirements contract (i.e., includes the Requirement clause at subsection 52.216-21 of the Federal Acquisition Regulation (FAR)), the Government is not required to order a part of any one requirement from the Contractor if that requirement exceeds the maximum-order limitations in paragraph (b) above.

(d)  Notwithstanding paragraphs (b) and (c) above, the Contractor shall honor any order exceeding the maximum order limitations in paragraph (b), unless that order (or orders) is returned to the ordering office within [Note to Contracting Officer: insert number] days after issuance, with written notice stating the contractor's intent not to ship the item (or items) called for and the reasons.  Upon receiving this notice, the Government may acquire the supplies or services from another source.

(End of clause)

I.5.	52.216-22    INDEFINITE QUANTITY (OCT 1995)

(a)  This is an indefinite-quantity contract for the supplies or services specified, and effective for the period stated, in the Schedule.  The quantities of supplies and services specified in the Schedule are estimates only and are not purchased by this contract.

(b)  Delivery or performance shall be made only as authorized by orders issued in accordance with the Ordering clause.  The Contractor shall furnish to the Government, when and if ordered, the supplies or services specified in the Schedule up to and including the quantity designated in the Schedule as the "maximum."  The Government shall order at least the quantity of supplies or services designated in the Schedule as the "minimum."

(c)  Except for any limitations on quantities in the Deliver-Order Limitations clause or in the Schedule, there is no limit on the number of orders that may be issued.  The Government may issue orders requiring delivery to multiple destinations or performance at multiple locations.

(d)  Any order issued during the effective period of this contract and not completed within that period shall be completed by the Contractor within the time specified in the order.  The contract shall govern the Contractor's and Government's rights and obligations with respect to that order to the same extent as if the order were completed during the contract's effective period; provided, that the Contractor shall not be required to make any deliveries under this contract 21 days after the contract termination date.

(End of clause)

I.6	52.217-8    OPTION TO EXTEND SERVICES (NOV 1999)

The Government may require continued performance of any services within the limits and at the rates specified in the contract.  The option provision may be exercised more than once, but the total extension of performance hereunder shall not exceed 6 months.  The Contracting Officer may exercise the option by written notice to the Contractor within the performance period of the contract.

(End of clause)

I.7	52.217-9    OPTION TO EXTEND THE TERM OF THE CONTRACT (MAR 	2000)

(a)  The Government may extend the term of this contract by written notice to the Contractor within the performance period of the contract or within 30 days after funds for the option year become available, whichever is later.

(b)  If the Government exercises this option, the extended contract shall be considered to include this option clause.

(c) The total duration of this contract, including the exercise of any options under this clause, shall not exceed 5 years.

(End of clause)

I.8	RESERVED

I.9	52.228-15    PERFORMANCE AND PAYMENT BONDS - CONSTRUCTION 	(OCT 2010)

(a)  As used in this clause-Contract-

“Original contract price” means the award price of the contract; or, for requirements contracts, the price payable for the estimated quantity; or, for indefinite-delivery type contracts, the price payable for the specified minimum quantity.  Original contract price does not include the price of any options, except those options exercised at the time of contract award.

(b)  Amount of required bonds.  Unless the resulting contract price is $250,000 or less, the successful offeror shall be required to furnish performance and payment bonds to the Contracting Officer as follows:

(l)  Performance Bonds (Standard Form 25).  The penal amount of performance bonds at the time of contract award shall be 20 percent of the original contract price.

(2)  Payment Bonds (Standard Form 25A) the penal amount of payment bonds shall be 20 percent of the original contract price.

(3)  Additional bond protection. (i) The Government may require additional performance and payment bond protection if the contract price is increased.  The increase in protection  generally will equal 20% of the increased in contract price.

- The Government may secure the additional protection by directing the Contractor to increase the penal amount of the existing bond or to obtain an additional bond.

(c)  Furnishing executed bonds.  The Contractor shall furnish all executed bonds, including any necessary reinsurance agreements, to the Contracting Officer, within the time period specified in the Bid Guarantee provision of the solicitation, or otherwise specified by the Contracting Officer, in any event, before starting work.

(d)  Surety or other security for bonds. The bonds shall be in the form of firm commitment, supported by corporate sureties whose names appear on the list contained in Treasury Department Circular 570, individual sureties, or by other acceptable security such as postal money order, certified check, cashier's check, irrevocable letter of credit, or bonds or notes of the United States.  Treasury Circular 570 is published in the Federal Register or Department of Treasury, Financial Management Service, Surety Bond Branch, 3700 East West Highway, Room 6F01, Hyattsville, MD 20782.  Or via the internet at http://www.fms.treas.gov/c570/c570.html.

(e)  Notice of subcontractor waiver of protection (40 U.S.C. 3133(c).  Any waiver of the right to sue on the payment bond is void unless it is in writing, signed by the person whose right is waived, and executed after such person has furnished labor or material for use in the performance of the contract.

(End of clause)

I.10	52.232-19     AVAILABILITY OF FUNDS FOR THE NEXT FISCAL YEAR.  	(APR 1984)

Funds are not presently available for performance under this contract beyond September 30 of the current calendar year.  The Government's obligation for performance of this contract beyond that date is contingent upon the availability of appropriated funds from which payment for contract purposes can be made.  No legal liability on the part of the Government for any payment may arise for performance under this contract beyond September 30 of the current calendar year, until funds are made available to the Contracting Officer for performance and until the Contractor receives notice of availability, to be confirmed in writing by the Contracting Officer.

(End of clause)

DEPARTMENT OF STATE ACQUISITION REGULATION (DOSAR) CLAUSES

I.11	652.204-70   DEPARTMENT OF STATE PERSONAL IDENTIFICATION 	CARD ISSUANCE PROCEDURES (MAY 2011)

(a) The Contractor shall comply with the Department of State (DOS) Personal Identification Card Issuance Procedures for all employees performing under this contract who require frequent and continuing access to DOS facilities, or information systems.  The Contractor shall insert this clause in all subcontracts when the subcontractor’s employees will require frequent and continuing access to DOS facilities, or information systems.

(b) The DOS Personal Identification Card Issuance Procedures may be accessed at http://www.state.gov/m/ds/rls/rpt/c21664.htm .

(End of clause)

I.12	652.243-70    NOTICES (AUG 1999)

Any notice or request relating to this contract given by either party to the other shall be in writing. Said notice or request shall be mailed or delivered by hand to the other party at the address provided in the schedule of the contract. All modifications to the contract must be made in writing by the Contracting Officer.

(End of clause)

I.13	652.242-73   AUTHORIZATION AND PERFORMANCE (AUG 1999)

(a)  The Contractor warrants the following:

- That is has obtained authorization to operate and do business in the country or countries in which this contract will be performed;

(2)  That is has obtained all necessary licenses and permits required to perform this contract; and,

(3)  That it shall comply fully with all laws, decrees, labor standards, and regulations of said country or countries during the performance of this contract.

(b) If the party actually performing the work will be a subcontractor or joint venture partner, then such subcontractor or joint venture partner agrees to the requirements of paragraph (a) of this clause.

(End of clause)

I.14	652.216-70	ORDERING - INDEFINITE-DELIVERY CONTRACT (APR 	2004)

The Government shall use one of the following forms to issue orders under this contract:

(a)	The Optional Form 347, Order for Supplies or Services, and Optional Form 348, Order for Supplies or Services Schedule - Continuation; or,

(b)	The DS-2076, Purchase Order, Receiving Report and Voucher, and DS-2077, Continuation Sheet.

(End of clause)

I.15	652.237-72	OBSERVANCE OF LEGAL HOLIDAYS AND 	ADMINISTRATIVE LEAVE  (APR 2004)

(a)  The Department of State observes the following days*as holidays:

New Year’s Day – US/ Zambian

Martin Luther King’s Birthday – US

Washington’s Birthday – US

Memorial Day- US/Zambian

Independence Day – US

Labor Day – US

Columbus Day – US

Veterans Day – US

Thanksgiving Day – US

Christmas Day US/Zambian

International Women’s Day – Zambian

Youth Day – Zambian

Good Friday – Zambian

Easter Monday – Zambian

Labour Day – Zambian

Independence – Zambian

Heroes Day – Zambian

Unity Day – Zambian

Farmer’s Day – Zambian

Day of national prayers - Zambian

*Any other day designated by Federal law, Executive Order, or Presidential Proclamation.

(b)  When any such day falls on a Saturday or Sunday, the following Monday is observed.  Observance of such days by Government personnel shall not be cause for additional period of performance or entitlement to compensation except as set forth in the contract. If the Contractor’s personnel work on a holiday, no form of holiday or other premium compensation will be reimbursed either as a direct or indirect cost, unless authorized pursuant to an overtime clause elsewhere in this contract.

(c)  When the Department of State grants administrative leave to its Government employees, assigned contractor personnel in Government facilities shall also be dismissed.  However, the Contractor agrees to continue to provide sufficient personnel to perform round-the-clock requirements of critical tasks already in operation or scheduled, and shall be guided by the instructions issued by the Contracting Officer or his/her duly authorized representative.

(d)  For fixed-price contracts, if services are not required or provided because the building is closed due to inclement weather, unanticipated holidays declared by the President, failure of Congress to appropriate funds, or similar reasons, deductions will be computed as follows:

(1)  The deduction rate in dollars per day will be equal to the per month contract price divided by 21 days per month.

- The deduction rate in dollars per day will be multiplied by the number of days services are not required or provided.

If services are provided for portions of days, appropriate adjustment will be made by the Contracting Officer to ensure that the Contractor is compensated for services provided.

- If administrative leave is granted to contractor personnel as a result of conditions stipulated in any “Excusable Delays” clause of this contract, it will be without loss to the Contractor. The cost of salaries and wages to the Contractor for the period of any such excused absence shall be a reimbursable item of direct cost hereunder for employees whose regular time is normally charged, and a reimbursable item of indirect cost for employees whose time is normally charged indirectly in accordance with the Contractor’s accounting policy.

(End of clause)

I.16	652.225-71    SECTION 8(A) OF THE EXPORT ADMINISTRATION ACT OF 	1979, as amended (AUG 1999)

(a)  Section 8(a) of the U.S. Export Administration Act of 1979, as amended (50 U.S.C. 2407(a)), prohibits compliance by U.S. persons with any boycott fostered by a foreign country against a country which is friendly to the United States and which is not itself the object of any form of boycott pursuant to United States law or regulation.  The Boycott of Israel by Arab League countries is such a boycott, and therefore, the following actions, if taken with intent to comply with, further, or support the Arab League Boycott of Israel, are prohibited activities under the Export Administration Act:

(1)  Refusing, or requiring any U.S. person to refuse to do business with or in Israel, with any Israeli business concern, or with any national or resident of Israel, or with any other person, pursuant to an agreement of, or a request from or on behalf of a boycotting country;

(2)  Refusing, or requiring any U.S. person to refuse to employ or otherwise discriminating against any person on the basis of race, religion, sex, or national origin of that person or of any owner, officer, director, or employee of such person;

(3) Furnishing information with respect to the race, religion, or national origin of any U.S. person or of any owner, officer, director, or employee of such U.S. person;

(4) Furnishing information about whether any person has, has had, or proposes to have any business relationship (including a relationship by way of sale, purchase, legal or commercial representation, shipping or other transport, insurance, investment, or supply) with or in the State of Israel, with any business concern organized

(5) under the laws of the State of Israel, with any Israeli national or resident, or with any person which is known or believed to be restricted from having any business relationship with or in Israel;

(6) Furnishing information about whether any person is a member of, has made contributions to, or is otherwise associated with or involved in the activities of any charitable or fraternal organization which supports the State of Israel; and,

(7) Paying, honoring, confirming, or otherwise implementing a letter of credit which contains any condition or requirement against doing business with the State of Israel.

(b) Under Section 8(a), the following types of activities are not forbidden ``compliance with the boycott,'' and are therefore exempted from Section 8(a)'s prohibitions listed in paragraphs (a)(1)-(6) above:

(1)	Complying or agreeing to comply with requirements:

(i)  Prohibiting the import of goods or services from Israel or goods produced or services provided by any business concern organized under the laws of Israel or by nationals or residents of Israel; or,

(ii)  Prohibiting the shipment of goods to Israel on a carrier of Israel, or by a route other than that prescribed by the boycotting country or the recipient of the shipment;

(2)	Complying or agreeing to comply with import and shipping document requirements with respect to the country of origin, the name of the carrier and route of shipment, the name of the supplier of the shipment or the name of the provider of other services, except that no information knowingly furnished or conveyed in response to such requirements may be stated in negative, blacklisting, or similar exclusionary terms, other than with respect to carriers or route of shipments as may be permitted by such regulations in order to comply with precautionary requirements protecting against war risks and confiscation;

(3)	Complying or agreeing to comply in the normal course of business with the unilateral and specific selection by a boycotting country, or national or resident thereof, of carriers, insurance, suppliers of services to be performed within the boycotting country or specific goods which, in the normal course of business, are identifiable by source when imported into the boycotting country;

(4)	Complying or agreeing to comply with the export requirements of the boycotting country relating to shipments or transshipments of exports to Israel, to any business concern of or organized under the laws of Israel, or to any national or resident of Israel;

(5)	Compliance by an individual or agreement by an individual to comply with the immigration or passport requirements of any country with respect to such individual or any member of such individual's family or with requests for information regarding requirements of employment of such individual within the boycotting country; and,

(6)	Compliance by a U.S. person resident in a foreign country or agreement by such person to comply with the laws of that country with respect to his or her activities exclusively therein, and such regulations may contain exceptions for such resident complying with the laws or regulations of that foreign country governing imports into such country of trademarked, trade named, or similarly specifically identifiable products, or components of products for his or her own use, including the performance of contractual services within that country, as may be defined by such regulations.

(End of clause)

I.17	652.229-71   PERSONAL PROPERTY DISPOSITION AT POSTS ABROAD 	(AUG 1999)

- The Contractor warrants the following:

(1)  That is has obtained authorization to operate and do business in the country or countries in which this contract will be performed;

(2)  That is has obtained all necessary licenses and permits required to perform this contract; and,

(3)  That it shall comply fully with all laws, decrees, labor standards, and regulations of said country or countries during the performance of this contract.

(b)	If the party actually performing the work will be a subcontractor or joint venture partner, then such subcontractor or joint venture partner agrees to the requirements of paragraph (a) of this clause.

(End of clause)

I.18 	CONTRACTOR IDENTIFICATION (JULY 2008)

Contract performance may require contractor personnel to attend meetings with government personnel and the public, work within government offices, and/or utilize government e-mail.

Contractor personnel must take the following actions to identify themselves as non-federal employees:

- Use an e-mail signature block that shows name, the office being supported and company affiliation (e.g. “John Smith, Office of Human Resources, ACME Corporation Support Contractor”);

- Clearly identify themselves and their contractor affiliation in meetings;

3)   Identify their contractor affiliation in Departmental e-mail and phone listings whenever contractor personnel are included in those listings; and

4)  Contractor personnel may not utilize Department of State logos or indicia on business cards.

(End of clause)

I.19 	652.229-70     EXCISE TAX EXEMPTION STATEMENT FOR 	CONTRACTORS WITHIN THE UNITED STATES (JULY 1988)

This is to certify that the item(s) covered by this contract is/are for export solely for the use of the U.S. Foreign Service Post identified in the contract schedule.

The Contractor shall use a photocopy of this contract as evidence of intent to export. Final proof of exportation may be obtained from the agent handling the shipment. Such proof shall be accepted in lieu of payment of excise tax.

(End of clause)

I.20 RECRUITMENT OF THIRD COUNTRY NATIONALS FOR PERFORMANCE ON DEPARTMENT OF STATE CONTRACTS (October 17, 2012)

1. On contracts exceeding $250,000 where performance will require the recruitment of non-professional third country nationals, the offeror is required to submit a Recruitment Plan as part of the proposal.  Contractors providing employer furnished housing are required to submit a Housing Plan.

2. Recruitment Plan

a. State the anticipated number of workers to be recruited, the skills they are expected to have, and the country or countries from which the Contractor intends to recruit them.

b. Explain how the Contractor intends to attract candidates and the recruitment strategy including the recruiter.

c. Provide sample recruitment agreement in English.

d. State in the offer that the recruited employee will not be charged recruitment or any similar fees. The Contractor or employer pays the recruitment fees for the worker if recruited by the Contractor or subcontractor to work specifically on Department of State jobs.

e. State in the offer that the Contractor’s recruitment practices comply with recruiting nation and host country labor laws.

f. State in the offer that the Contractor has read and understands the requirements of FAR 52.222-50 Combating Trafficking in Persons.

g. Contractor and subcontractors shall only use bona fide licensed recruitment companies. Recruitment companies shall only use bona fide employees and not independent agents.

h. Contractor will advise the Contracting Officer of any changes to the Recruitment Plan during performance.

3. The offeror will submit a Housing Plan if the Contractor intends to provide employer furnished housing for TCNs.  The Housing Plan must describe the location and description of the proposed housing.  Contractors must state in their offer that housing meets host country housing and safety standards and local codes or explain any variance.  Contractor shall comply with any Temporary Labor Camp standards contained in this contract.  In contracts without a Temporary Labor Camp standard, fifty square feet is the minimum amount of space per person without a Contracting Officer waiver.  Contractor shall submit proposed changes to their Housing Plan to the Contracting Officer for approval.

4. Department of State contractor and subcontractors will treat employees with respect and dignity by taking the following actions:

a. Contractor may not hold employee passports and other identification documents longer than 48 hours without employee concurrence.  Contractors and subcontractors are reminded of the prohibition contained in Title 18, United States Code, Section 1592, against knowingly destroying, concealing, removing, confiscating, or possessing any actual or purported passport or other immigration document to prevent or restrict the person’s liberty to move or travel in order to maintain the services of that person, when the person is or has been a victim of a severe form of trafficking in persons.

b. Contractor shall provide employees with signed copies of the/their employment contracts, in English and the employee’s native language, that define the terms of employment, compensation, job description, and benefits.  Contracts must be provided prior to employee departure from their countries of origin.

c. Contractor shall provide all employees with a “Know Your Rights” brochure and document that employees have been briefed on the contents of the brochure.  The English language version is available at http://www.state.gov/j/tip or from the Contracting Officer.

d. Contractor shall brief employees on the requirements of the FAR 52.222-50 Combating Trafficking in Persons including the requirements against commercial sex even in countries where it is legal and shall provide a copy of the briefing to the Contracting Officer Representative (COR).

e. Contractor shall display posters in worker housing advising employees in English and the dominant language of the Third Country Nationals being housed of the requirement to report violations of Trafficking in Persons to the company and the company’s obligation to report to the Contracting Officer.  The poster shall also indicate that reports can also be submitted to the Office of the Inspector General (OIG) Hotline at 202-647-3320 or 1-800-409-9926 or via e-mail at OIGHotline@state.gov.

f. Contractor and subcontractors shall comply with sending and receiving nation laws regarding transit, entry, exit, visas, and work permits. Contractors are responsible for repatriation of workers imported for contract performance.

g. Contractor will monitor subcontractor compliance at all tiers. This includes verification that subcontractors are aware of, and understand, the requirements of FAR 52.222-50 Combating Trafficking in Persons and this clause.  Contractors specifically agree to allow U.S. Government personnel access to contractor and subcontractor personnel, records, and housing for audit of compliance with these requirements.

h. The Contractor agrees to include this clause in all subcontracts over $250,000 involving recruitment of third country national for subcontractor performance.

SECTION J - LIST OF DOCUMENTS, EXHIBITS AND OTHER ATTACHMENTS

Exhibit 1		List of Currently Held Residential Properties

Exhibit 2		Sample Task Order Form

Exhibit 3	List of Properties Requiring Make-Ready Services in the Previous Calendar Year

Exhibit 4		Technical Specifications and Checklists

Exhibit 5		Government Furnished Property

Exhibit 6		Sample Monthly Report Form

# Exhibit 7		Contractor Furnished Property

Exhibit 8		Sample Bank Letter of Guaranty

Exhibit 1 - List of Currently Held Residential Properties

| No. | Location Property ID | Qty | Estimated Area | Scheduled Hours | Escort |
| --- | --- | --- | --- | --- | --- |
| 1 | 6019 | 1 | 47 | 8 | yes |
| 2 | 6020 | 1 | 47 | 8 | yes |
| 3 | 24026 | 1 | 50 | 8 | yes |
| 4 | 9021 | 1 | 57 | 8 | yes |
| 5 | 8015 | 1 | 72 | 8 | yes |
| 6 | 7017 | 1 | 77 | 8 | yes |
| 7 | 98593 | 1 | 111 | 8 | yes |
| 8 | 24028 | 1 | 115 | 8 | yes |
| 9 | 24036 | 1 | 101 | 8 | yes |
| 10 | 8012 | 1 | 131 | 8 | yes |
| 11 | 2013 | 1 | 123 | 8 | yes |
| 12 | 11015 | 1 | 174 | 8 | yes |
| 13 | 17030 | 1 | 174 | 8 | yes |
| 14 | 98566 | 1 | 160 | 8 | yes |
| 15 | 141 | 1 | 180 | 8 | yes |
| 16 | 142 | 1 | 180 | 8 | yes |
| 17 | 143 | 1 | 180 | 8 | yes |
| 18 | 144 | 1 | 180 | 8 | yes |
| 19 | 10014 | 1 | 171 | 8 | yes |
| 20 | 1232 | 1 | 170 | 8 | yes |
| 21 | 1223 | 1 | 170 | 8 | yes |
| 22 | 147 | 1 | 170 | 8 | yes |
| 23 | 1222 | 1 | 175 | 8 | yes |
| 24 | 146 | 1 | 170 | 8 | yes |
| 25 | 1226 | 1 | 170 | 8 | yes |
| 26 | 6010 | 1 | 200 | 8 | yes |
| 27 | 98598 | 1 | 150 | 8 | yes |
| 28 | 137 | 1 | 158 | 8 | yes |
| 29 | 65 | 1 | 180 | 8 | yes |
| 30 | 1157 | 1 | 180 | 8 | yes |
| 31 | 1153 | 1 | 180 | 8 | yes |
| 32 | 1156 | 1 | 180 | 8 | yes |
| 33 | 1154 | 1 | 180 | 8 | yes |
| 34 | 27032 | 1 | 200 | 8 | yes |
| 35 | 98532 | 1 | 170 | 8 | yes |
| 36 | 160 | 1 | 229 | 8 | yes |
| 37 | 166 | 1 | 166 | 8 | yes |
| 38 | 175 | 1 | 219 | 8 | yes |
| 39 | 176 | 1 | 219 | 8 | yes |
| 40 | 174 | 1 | 219 | 8 | yes |
| 41 | 159 | 1 | 180 | 8 | yes |
| 42 | 168 | 1 | 185 | 8 | yes |
| 43 | 16021 | 1 | 238 | 8 | yes |
| 44 | 162 | 1 | 191 | 8 | yes |
| 45 | 163 | 1 | 191 | 8 | yes |
| 46 | 61 | 1 | 191 | 8 | yes |
| 47 | 17022 | 1 | 213 | 8 | yes |
| 48 | 98595 | 1 | 248 | 8 | yes |
| 49 | 26031 | 1 | 171 | 8 | yes |
| 50 | 158 | 1 | 212 | 8 | yes |
| 51 | 98538 | 1 | 237 | 8 | yes |
| 52 | 167 | 1 | 186 | 8 | yes |
| 53 | 157 | 1 | 211 | 8 | yes |
| 54 | 150 | 1 | 203 | 8 | yes |
| 55 | 148 | 1 | 203 | 8 | yes |
| 56 | 9013 | 1 | 184 | 8 | yes |
| 57 | 155 | 1 | 235 | 8 | yes |
| 58 | 35 | 1 | 206 | 8 | yes |
| 59 | 19024 | 1 | 280 | 8 | yes |
| 60 | 12017 | 1 | 227 | 8 | yes |
| 61 | 165 | 1 | 251 | 8 | yes |
| 62 | 171 | 1 | 249 | 8 | yes |
| 63 | 172 | 1 | 249 | 8 | yes |
| 64 | 4 | 1 | 256 | 8 | yes |
| 65 | 25030 | 1 | 280 | 8 | yes |
| 66 | 235 | 1 | 336 | 8 | yes |
| 67 | 130 | 1 | 336 | 8 | yes |
| 68 | 129 | 1 | 336 | 8 | yes |
| 69 | 234 | 1 | 336 | 8 | yes |
| 70 | 134 | 1 | 336 | 8 | yes |
| 71 | 140 | 1 | 336 | 8 | yes |
| 72 | 132 | 1 | 336 | 8 | yes |
| 73 | 131 | 1 | 336 | 8 | yes |
| 74 | 138 | 1 | 249 | 8 | yes |
| 75 | 9 | 1 | 275 | 8 | yes |
| 76 | 98561 | 1 | 226 | 8 | yes |
| 77 | 5008 | 1 | 233 | 8 | yes |
| 78 | 111 | 1 | 267 | 8 | yes |
| 79 | 169 | 1 | 290 | 8 | yes |
| 80 | 7011 | 1 | 309 | 8 | yes |
| 81 | 2 | 1 | 347 | 8 | yes |
| 82 | 100 | 1 | 260 | 8 | yes |
| 83 | 112 | 1 | 252 | 8 | yes |
| 84 | 156 | 1 | 260 | 8 | yes |
| 85 | 136 | 1 | 249 | 8 | yes |
| 86 | 154 | 1 | 289 | 8 | yes |
| 87 | 20025 | 1 | 419 | 8 | yes |
| 88 | 149 | 1 | 385 | 8 | yes |
| 89 | 15020 | 1 | 400 | 8 | yes |
| 90 | 2005 | 1 | 426 | 8 | yes |

| Total Square Meters | 19,486 |  | Sq. Meters |
| --- | --- | --- | --- |
| All Areas |  |  |

Exhibit 2 - Sample Task Order Form

Task Order # _______		Approval:    		Page 1 of

________________________________________________________________________

Requestor:  _________		Telephone #:		Priority

________________________________________________________________________

Property #__________		Equipment:		Requested Date:

or address__________					Due:

Unit:								Shop:

________________________________________________________________________

Task #				Description

Approved: _____________	Reviewed by: _________	Printed by: ______________

Customer Signature :

Comments:

Worker's Name				Worker's ID:

Worker's Signature:				Completion Date:

FOR MAJOR REPAIRS ONLY:

Work: ________OT: ________Travel:_______OT: ________Wait: ______OT:______

Materials used (use other side as needed):

Exhibit 3 - List of Properties Requiring Make-Ready Services in the Previous Calendar Year

| Item | Property Address | Type of work | Estimate Average Volume (m²) |
| --- | --- | --- | --- |
| 1 | Dream Valley | Painting, Carpentry, Electrical, plumbing work and HVAC | 210 |
| 2 | Musikili Unit 3 | Painting, carpentry, Electrical, plumbing work and HVAC | 180 |
| 3 | Ibex Hill #4 | Painting, carpentry, Electrical, plumbing work and HVAC | 174 |
| 4 | Orchards unit 1 | Carpentry, Electrical, plumbing work and HVAC | 211 |
| 5 | 33S/1 Mutende | Carpentry, Electrical, plumbing work and HVAC | 212 |
| 6 | 33S/2 Mutende | Carpentry, Electrical, plumbing work and HVAC | 212 |
| 7 | Musikili Park # 3 | Painting, carpentry, Electrical, plumbing work and HVAC | 184 |
| 8 | Ekaya 6 | Carpentry, Electrical, plumbing work and HVAC | 212 |
| 9 | Musikili Park # 4 | Painting, carpentry, Electrical, plumbing work and HVAC | 184 |
| 10 | Orchards 2 | Carpentry, Electrical, plumbing work and HVAC | 211 |
| 11 | Rosewood 1 | Carpentry, Electrical, plumbing work and HVAC | 227 |
| 12 | Rosewood 8 | Carpentry, Electrical, plumbing work and HVAC | 227 |
| 13 | Orchards 3 | Carpentry, Electrical, plumbing work and HVAC | 211 |
| 14 | Rosewood 4 | Carpentry, Electrical, plumbing work and HVAC | 227 |
| 15 | 31A Mutende | Carpentry, Electrical, plumbing work and HVAC | 256 |
| 16 | Reedbuck 2 | Carpentry, Electrical, plumbing work and HVAC | 174 |
| 17 | 15E Roan | Painting, carpentry, Electrical, plumbing work and HVAC | 175 |
| 18 | 29B Leopards Hill RD | Painting, carpentry, Electrical, plumbing work and HVAC | 184 |
| 19 | 55 Kabulonga | Painting, carpentry, Electrical, plumbing work and HVAC | 237 |

Exhibit 4 - Technical Specifications and Checklists

Plumbing Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Faucets are in good serviceable condition |  |  |
| No leaks detected |  |  |
| Hot and cold water checked |  |  |
| Shutoff valve for water is identified |  |  |
| All valves labeled and functioning properly |  |  |
| Drain is working correctly |  |  |
| Flushing mechanism for toilets is working correctly |  |  |
| Shower head mounted and functioning correctly |  |  |
| Yard taps are all functioning correctly |  |  |
| Booster pump is in good and serviceable condition |  |  |

Electrical Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Lights function correctly |  |  |
| All outlets are properly grounded and wired correctly |  |  |
| All outlets function correctly and are in good and serviceable condition |  |  |
| All security light electrical connections are good and located inside approved enclosures |  |  |
| All photo cells are functioning correctly |  |  |
| All security lights are in good and serviceable condition and functioning correctly |  |  |
| Distribution panels properly wired, labeled, has a dead front panel and all open breaker spaces blanked |  |  |

HVAC Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| AC control securely affixed to wall in room of unit |  |  |
| Indoor and Outdoor Units has been cleaned and serviced |  |  |
| Indoor Unit functions in all modes properly |  |  |
| Refrigerant added |  |  |
| All wiring and piping securely fasten to supporting structure |  |  |

Carpentry Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Door/window opens and closes properly |  |  |
| Door locks are secure and operate easily |  |  |
| Glass is clean and free of cracks and chips |  |  |
| Fly screen mesh is free of rips or holes |  |  |
| Two complete sets of keys for all locks on door |  |  |
| Shelves all present and are securely supported |  |  |
| Drawers operate properly and are securely supported |  |  |
| Door does not stick or bind at jamb or floor |  |  |
| Fly screen mesh is securely mounted to frame |  |  |
| Ceiling is in good and serviceable condition |  |  |

Roofing Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Roof structure sound and secure |  |  |
| Gutters properly installed |  |  |
| Fascial board sound and neat No roof leaks detected |  |  |
| No broken roof sheets |  |  |

Demolition Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| All utilities disconnected before commencement of demo works |  |  |
| All debris removed from site |  |  |
| All fixtures and fitting secured and protected |  |  |
| Proper safety plan in place |  |  |

Masonry Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Wall is clean and in serviceable condition |  |  |
| No holes or cracks visible |  |  |
| Nails and other devices for hanging pictures or other items have been removed |  |  |
| Floor surface is structurally sound and there are no loose components or protruding materials |  |  |
| Wall is clean and in serviceable condition |  |  |

General Mechanical Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Door stoppers installed |  |  |
| Pool Gate(s) swing outwards away from pool area |  |  |
| Pool Gate(s) have functioning self-latching and lockable hardware |  |  |
| All fixed security grills securely mounted to supporting structure |  |  |
| Security grill locks are secure and operate easily |  |  |

Safety Equipment Services Check List

| Item | Completed | Notes |
| --- | --- | --- |
| Fire Extinguisher Mounted and is readily accessible |  |  |
| Smoke/CO detector is installed |  |  |
| Smoke/CO detector is in good and functioning condition |  |  |

Exhibit 5 - Government Furnished Property (GFP)

The Government shall provide all the following materials:

| Name of Materials | Quantity | Remarks |
| --- | --- | --- |
| Water Heaters | 20 per year |  |
| Air Conditioners | 60 per year |  |
| Ceiling Fans | 50 per year |  |
| Distillers | 10 per year |  |
| Carbon Monoxide Sensor | 20 per year |  |
| Smoke Detectors | 50 per year |  |
| Dead bolt locks | 30 per year |  |

Exhibit 6 - Monthly Report

Monthly Report for the Month of _____________

U.S. EMBASSY, ___________

1.	Services Requested During the Month:

| Task Order | Location/Description | Dates | Status |
| --- | --- | --- | --- |

2.	Other Notes (include task order number):

A.	Problems Encountered:

B.	Major Repairs Needed:

C.	Major Repairs Made:

D.	Recommendations:

Signed by_________________________      Date _____________________

Exhibit 7 - Contractor Furnished Property

The Contractor shall use only environmentally-preferred chemical cleaning products.  The Contractor shall identify products by brand name for each of the following product types:

| (a) Glass cleaner: |  |
| --- | --- |
| (b) Furniture polish: |  |
| (c) Floor stripper: |  |
| (d) Floor finisher: |  |
| (e) Carpet cleaner: |  |
| (f) Solvent spotter: |  |
| (g) Gum remover: |  |
| (h) Wood floor finish: |  |
| (i) Bathroom hand cleaner/soap: |  |
| (j) Bathroom disinfectant: |  |
| (k) Bathroom cleaner: |  |
| (l) Bathroom deodorizers: |  |
| (m) Urinal deodorizers: |  |
| (n) Lime and scale remover: |  |

In addition, the Contractor shall provide following non-chemical products containing the maximum feasible amount of recovered materials:

(1)	Bathroom Tissue - The bathroom tissue must contain at least 100% recovered materials and 50% post-consumer content.

(2)	Toilet Seat Covers - Toilet seat covers must contain at least 100% recovered materials and 50% post-consumer content.

(3)	Paper Towels - The paper towels must contain at least 100% recovered materials and 40% post-consumer content.

(4)	General Purpose Industrial Wipes - The general purpose industrial wipes must contain at least 100% recovered materials and 40% post-consumer content.

(5)	Plastic Trash Bags - Plastic trash bags must contain at least 25% post-consumer content.

Information on environmentally preferable products (EPP) is available on the Internet at http://www.gsa.gov/portal/category/27119.

All non-chemical products (paper, plastic, etc.) should conform to the Environmental Protection Agency (EPA) Comprehensive Procurement Guidelines (CPG) if the products are CPG-designated items.  CPG information is available on the Internet at http://www.epa.gov/cpg.

Contractors may propose more than one product within a product category and/or propose a product or products addressing more than one product category.

Once this list of products has been approved by the Contracting Officer, the Contractor is responsible for using only those approved cleaning chemical products in the building.  If for some reason the product is found later to be ineffective and the Contractor would otherwise like to propose an alternative product, or the Contracting Officer would like to propose a more environmentally-preferable product, either the Contractor or Contracting Officer may propose for consideration an “equal” product.  If the parties agree to the replacement product, the contract will be modified.

# Exhibit 8 - SAMPLE LETTER OF BANK GUARANTY

Place [         ]

Date [          ]

Contracting Officer

U.S. Embassy, [Post name]

[Mailing Address]

Letter of Guaranty No. _______

SUBJECT: Performance and Guaranty

The Undersigned, acting as the duly authorized representative of the bank, declares that the bank hereby guarantees to make payment to the Contracting Officer by check made payable to the Treasurer of the United States, immediately upon notice, after receipt of a simple written request from the Contracting Officer, immediately and entirely without any need for the Contracting Officer to protest or take any legal action or obtain the prior consent of the Contractor to show any other proof, action, or decision by an other authority, up to the sum of [amount equal to 20% of the contract price in U.S. dollars during the period ending with the date of final acceptance and 10% of the contract price during contract guaranty period], which represents the deposit required of the Contractor to guarantee fulfillment of his obligations for the satisfactory, complete, and timely performance of the said contract [contract number] for [description of work] at [location of work] in strict compliance with the terms, conditions and specifications of said contract, entered into between the Government and [name of contractor] of [address of contractor] on [contract date], plus legal charges of 10% per annum on the amount called due, calculated on the sixth day following receipt of the Contracting Officer’s written request until the date of payment.

The undersigned agrees and consents that said contract may be modified by Change Order or Supplemental Agreement affecting the validity of the guaranty provided, however, that the amount of this guaranty shall remain unchanged.

The undersigned agrees and consents that the Contracting Officer may make repeated partial demands on the guaranty up to the total amount of this guaranty, and the bank will promptly honor each individual demand.

This letter of guaranty shall remain in effect until 3 months after completion of the guaranty period of Contract requirement.

| Depository Institution: | [name] |
| --- | --- |
| Address: |  |
| Representatives: |  |  | Location: |  |
|  |  | State of Inc.: |  |
|  |  | Corporate Seal: |
| Certificate of Authority is attached evidencing authority of the signer to bind the bank to this document. |

SECTION K - REPRESENTATIONS, CERTIFICATIONS, AND OTHER STATEMENTS OF OFFERORS

K.1	52.203-2    CERTIFICATE OF INDEPENDENT PRICE DETERMINATION. 	(APR 1985)

(a)  The offeror certifies that -

(1)  The prices in this offer have been arrived at independently, without, for the purpose of restricting competition, any consultation, communication, or agreement with any other offeror or competitor relating to (i) those prices, (ii) the intention to submit an offer, or (iii) the methods or factors used to calculate the prices offered;

(2)  The prices in this offer have not been and will not be knowingly disclosed by the offeror, directly or indirectly, to any other offeror or competitor before bid opening (in the case of a sealed bid solicitation) or contract award (in the case of a negotiated solicitation) unless otherwise required by law; and

(3)  No attempt has been made or will be made by the offeror to induce any other concern to submit or not to submit an offer for the purpose of restricting competition.

(b)  Each signature on the offer is considered to be a certification by the signatory that the signatory -

(1)  Is the person in the offeror's organization responsible for determining the prices being offered in this bid or proposal, and that the signatory has not participated and will not participate in any action contrary to subparagraphs (a)(1) through (a)(3) above; or

(2)  (i)	Has been authorized, in writing, to act as agent for the following principals in certifying that those principals have not participated, and will not participate in any action contrary to subparagraphs (a)(1) through (a)(3) above ____________________________________________________________  insert full name of person(s) in the offeror's organization responsible for determining the prices offered in this bid or proposal, and the title of his or her position in the offeror's organization];

(ii)  As an authorized agent, does certify that the principals named in subdivision (b)(2)(i) above have not participated, and will not participate, in any action contrary to subparagraphs (a)(1) through (a)(3) above; and

(iii)  As an agent, has not personally participated, and will not participate, in any action contrary to subparagraphs (a)(1) through (a)(3) above.

(c)  If the offeror deletes or modifies subparagraph (a)(2) above, the offeror must furnish with its offer a signed statement setting forth in detail the circumstances of the disclosure.

K.2	52.203-11    CERTIFICATION AND DISCLOSURE REGARDING PAYMENTS TO INFLUENCE CERTAIN FEDERAL TRANSACTIONS (SEPT 2007)

(a)	Definitions.  As used in this provision – “Lobbying contact” has the meaning provided at 2 USC 1602(8).  The terms “agency”, “influencing or attempting to influence”, “officer or employee of an agency”, “person”, “reasonable compensation”, and “regularly employed” are defined in the FAR clause of this solicitation entitled  Limitation on Payments to Influence Certain Federal Transactions (52.203-12).

(b) 	Prohibition.  The prohibition and exceptions contained in the FAR clause of this solicitation entitled “Limitation on Payments to Influence Certain Federal Transactions” (52.203-12) are hereby incorporated by reference in this provision.

.

(c)	Certification.  The offeror, by signing its offer, hereby certifies to the best of his or her knowledge and belief that no Federal appropriated funds have been paid or will be paid to any person for influencing or attempting to influence an officer or employee of any agency, a Member of Congress, an officer or employee of Congress, or an employee   of a member of Congress on its behalf in connection with the awarding of this contract.

(d) 	Disclosure.  If any registrants under the Lobbying Disclosure Act of 1995 have made a lobbying contract on behalf of the offeror with respect to this contract, the offeror shall complete and submit, with its officer, OMB Standard Form LLL, Disclosure of Lobbying Activities, to provide the name of the registrants.  The offeror need not report regularly employed officers or employees of the offeror to whom payments of reasonable compensation were made.

(e)	Penalty.  Submission of this certification and disclosure is a prerequisite for making or entering into this contract imposed by 31 USC 1352.  Any persons who makes an expenditure prohibited under this provision or who fails to file or amend the disclosure required to be filed or amended by this provision, shall be subject to a civil penalty of not less than $10,000, and not more than $250,000, for each failure.

K.3	52.204-3    TAXPAYER IDENTIFICATION (OCT 98)

(a)  Definitions

"Common parent", as used in this provision, means that corporate entity that owns or controls an affiliated group of corporations that files its Federal income tax returns on a consolidated basis, and of which the offeror is a member.

"Taxpayer Identification Number (TIN)", as used in this provision, means the number required by the IRS to be used by the offeror in reporting income tax and other returns.  The TIN may be either a Social Security Number or an Employer Identification Number.

(b)  All offerors must submit the information required in paragraphs (d) through (f) of this provision in order to comply with debt collection requirements of 31 U.S.C. 7701(c) and 3325 (d), reporting requirements of 26 USC 6041, 6041A, and 6050M and implementing regulations issued by the Internal Revenue Service (IRS).  If the resulting contract is subject to the reporting requirements described in FAR 4.904, the failure or refusal by the offeror to furnish the information may result in a 31 percent reduction of payments otherwise due under the contract.

(c)  The TIN may be used by the Government to collect and report on any delinquent amounts arising out of the offeror’s relationship with the Government (3l USC 7701( c)(3)).  If the resulting contract is subject to the payment reporting requirements described in FAR 4.904, the TIN provided hereunder may be matched with IRS records to verify the accuracy of the offeror’s TIN.

(d)  Taxpayer Identification Number (TIN)

| TIN: |
| --- |
|  | TIN has been applied for |
|  | TIN is not required because: |
|  | Offeror is a nonresident alien, foreign corporation, or foreign partnership that does not have income effectively connected with the conduct of a trade or business in the U.S. and does not have an office or place of business or a fiscal paying agent in the U.S. |
|  | Offeror is an agency or instrumentality of a foreign government |
|  | Offeror is an agency or instrumentality of the Federal Government |

(e) Type of Organization

|  | Sole Proprietorship |
| --- | --- |
|  | Partnership |
|  | Corporate Entity (not tax exempt) |
|  | Corporate Entity (tax exempt) |
|  | Government entity (Federal, State or local) |
|  | Foreign Government |
|  | International organization per 26 CFR 1.6049-4 |
|  | Other: |

(f) Common Parent

|  | Offeror is not owned or controlled by a common parent as defined in paragraph (a) of this clause. |
| --- | --- |
|  | Name and TIN of common parent |
| Name |  |
| TIN |  |

(End of provision)

### K.4.  52.204-8 Annual Representations and Certifications. (Jan 2018)

(a)(1) The North American Industry Classification System (NAICS) code for this acquisition is 238990.

(2) The small business size standard is $14M.

(3) The small business size standard for a concern which submits an offer in its own name, other than on a construction or service contract, but which proposes to furnish a product which it did not itself manufacture, is 500 employees.

(b)(1) If the provision at 52.204-7, System for Award Management, is included in this solicitation, paragraph (d) of this provision applies.

(2) If the provision at 52.204-7 is not included in this solicitation, and the offeror is currently registered in the System for Award Management (SAM), and has completed the Representations and Certifications section of SAM electronically, the offeror may choose to use paragraph (d) of this provision instead of completing the corresponding individual representations and certifications in the solicitation. The offeror shall indicate which option applies by checking one of the following boxes:

□ (i) Paragraph (d) applies.

□ (ii) Paragraph (d) does not apply and the offeror has completed the individual representations and certifications in the solicitation.

(c)(1) The following representations or certifications in SAM are applicable to this solicitation as indicated:

(i) 52.203-2, Certificate of Independent Price Determination. This provision applies to solicitations when a firm-fixed-price contract or fixed-price contract with economic price adjustment is contemplated, unless—

(A) The acquisition is to be made under the simplified acquisition procedures in Part 13;

(B) The solicitation is a request for technical proposals under two-step sealed bidding procedures; or

(C) The solicitation is for utility services for which rates are set by law or regulation.

(ii) 52.203-11, Certification and Disclosure Regarding Payments to Influence Certain Federal Transactions. This provision applies to solicitations expected to exceed $250,000.

(iii) 52.203-18, Prohibition on Contracting with Entities that Require Certain Internal Confidentiality Agreements or Statements-Representation. This provision applies to all solicitations.

(iv) 52.204-3, Taxpayer Identification. This provision applies to solicitations that do not include the provision at 52.204-7, System for Award Management.

(v) 52.204-5, Women-Owned Business (Other Than Small Business). This provision applies to solicitations that—

(A) Are not set aside for small business concerns;

(B) Exceed the simplified acquisition threshold; and

(C) Are for contracts that will be performed in the United States or its outlying areas.

(vi) 52.209-2, Prohibition on Contracting with Inverted Domestic Corporations—Representation.

(vii) 52.209-5, Certification Regarding Responsibility Matters. This provision applies to solicitations where the contract value is expected to exceed the simplified acquisition threshold.

(viii) 52.209-11, Representation by Corporations Regarding Delinquent Tax Liability or a Felony Conviction under any Federal Law. This provision applies to all solicitations.

(ix) 52.214-14, Place of Performance—Sealed Bidding. This provision applies to invitations for bids except those in which the place of performance is specified by the Government.

(x) 52.215-6, Place of Performance. This provision applies to solicitations unless the place of performance is specified by the Government.

(xi) 52.219-1, Small Business Program Representations (Basic & Alternate I). This provision applies to solicitations when the contract will be performed in the United States or its outlying areas.

(A) The basic provision applies when the solicitations are issued by other than DoD, NASA, and the Coast Guard.

(B) The provision with its Alternate I applies to solicitations issued by DoD, NASA, or the Coast Guard.

(xii) 52.219-2, Equal Low Bids. This provision applies to solicitations when contracting by sealed bidding and the contract will be performed in the United States or its outlying areas.

(xiii) 52.222-22, Previous Contracts and Compliance Reports. This provision applies to solicitations that include the clause at 52.222-26, Equal Opportunity.

(xiv) 52.222-25, Affirmative Action Compliance.This provision applies to solicitations, other than those for construction, when the solicitation includes the clause at 52.222-26, Equal Opportunity.

(xv) 52.222-38, Compliance with Veterans’ Employment Reporting Requirements. This provision applies to solicitations when it is anticipated the contract award will exceed the simplified acquisition threshold and the contract is not for acquisition of commercial items.

(xvi) 52.223-1, Biobased Product Certification. This provision applies to solicitations that require the delivery or specify the use of USDA–designated items; or include the clause at 52.223-2, Affirmative Procurement of Biobased Products Under Service and Construction Contracts.

(xvii) 52.223-4, Recovered Material Certification. This provision applies to solicitations that are for, or specify the use of, EPA–designated items.

(xviii) 52.223-22, Public Disclosure of Greenhouse Gas Emissions and Reduction Goals–Representation. This provision applies to solicitation that include the clause at 52.204-7.

(xix) 52.225-2, Buy American Certificate. This provision applies to solicitations containing the clause at 52.225-1.

(xx) 52.225-4, Buy American—Free Trade Agreements—Israeli Trade Act Certificate. (Basic, Alternates I, II, and III.) This provision applies to solicitations containing the clause at 52.225-3.

(A) If the acquisition value is less than $25,000, the basic provision applies.

(B) If the acquisition value is $25,000 or more but is less than $50,000, the provision with its Alternate I applies.

(C) If the acquisition value is $50,000 or more but is less than $80,317, the provision with its Alternate II applies.

(D) If the acquisition value is $80,317 or more but is less than $100,000, the provision with its Alternate III applies.

(xxi) 52.225-6, Trade Agreements Certificate. This provision applies to solicitations containing the clause at 52.225-5.

(xxii) 52.225-20, Prohibition on Conducting Restricted Business Operations in Sudan—Certification. This provision applies to all solicitations.

(xxiii) 52.225-25, Prohibition on Contracting with Entities Engaging in Certain Activities or Transactions Relating to Iran-Representation and Certifications. This provision applies to all solicitations.

(xxiv) 52.226-2, Historically Black College or University and Minority Institution Representation. This provision applies to solicitations for research, studies, supplies, or services of the type normally acquired from higher educational institutions.

(2) The following representations or certifications are applicable as indicated by the Contracting Officer:

[Contracting Officer check as appropriate.]

__ (i) 52.204-17, Ownership or Control of Offeror.

__ (ii) 52.204-20, Predecessor of Offeror.

__ (iii) 52.222-18, Certification Regarding Knowledge of Child Labor for Listed End Products.

__ (iv) 52.222-48, Exemption from Application of the Service Contract Labor Standards to Contracts for Maintenance, Calibration, or Repair of Certain Equipment- Certification.

__ (v) 52.222-52, Exemption from Application of the Service Contract Labor Standards to Contracts for Certain Services-Certification.

__ (vi) 52.223-9, with its Alternate I, Estimate of Percentage of Recovered Material Content for EPA–Designated Products (Alternate I only).

__ (vii) 52.227-6, Royalty Information.

__ (A) Basic.

__(B) Alternate I.

__ (viii) 52.227-15, Representation of Limited Rights Data and Restricted Computer Software.

(d) The offeror has completed the annual representations and certifications electronically via the SAM website accessed through https://www.acquisition.gov. After reviewing the SAM database information, the offeror verifies by submission of the offer that the representations and certifications currently posted electronically that apply to this solicitation as indicated in paragraph (c) of this provision have been entered or updated within the last 12 months, are current, accurate, complete, and applicable to this solicitation (including the business size standard applicable to the NAICS code referenced for this solicitation), as of the date of this offer and are incorporated in this offer by reference (see FAR 4.1201); except for the changes identified below [offeror to insert changes, identifying change by clause number, title, date]. These amended representation(s) and/or certification(s) are also incorporated in this offer and are current, accurate, and complete as of the date of this offer.

FAR Clause # Title Date Change

____________ _________ _____ _______

Any changes provided by the offeror are applicable to this solicitation only, and do not result in an update to the representations and certifications posted on SAM.

(End of provision)

K.5  RESERVED

K.6	52.209-5    Certification Regarding Responsibility Matters (oct 2015)

(a) (1) The Offeror certifies, to the best of its knowledge and belief, that --

(i) The Offeror and/or any of its Principals --

(A) Are [_] are not [_] presently debarred, suspended, proposed for debarment, or declared ineligible for the award of contracts by any Federal agency;

(B) Have [_] have not [_], within a three-year period preceding this offer, been convicted of or had a civil judgment rendered against them for: commission of fraud or a criminal offense in connection with obtaining, attempting to obtain, or performing a public (Federal, State, or local) contract or subcontract; violation of Federal or State antitrust statutes relating to the submission of offers; or commission of embezzlement, theft, forgery, bribery, falsification or destruction of records, making false statements, tax evasion, violating Federal criminal tax laws, or receiving stolen property (if offeror checks “have”, the offeror shall also see 52.209-7, if included in this solicitation); and

(C) Are [_] are not [_] presently indicted for, or otherwise criminally or civilly charged by a governmental entity with, commission of any of the offenses enumerated in paragraph (a)(1)(i)(B) of this provision; and

(D) Have [_], have not [_], within a three-year period preceding this offer, been notified of any delinquent Federal taxes in an amount that exceeds $3,500 for which the liability remains unsatisfied.

(1) Federal taxes are considered delinquent if both of the following criteria apply:

(i) The tax liability is finally determined. The liability is finally determined if it has been assessed. A liability is not finally determined if there is a pending administrative or judicial challenge. In the case of a judicial challenge to the liability, the liability is not finally determined until all judicial appeal rights have been exhausted.

(ii) The taxpayer is delinquent in making payment. A taxpayer is delinquent if the taxpayer has failed to pay the tax liability when full payment was due and required. A taxpayer is not delinquent in cases where enforced collection action is precluded.

(2) Examples.

(i) The taxpayer has received a statutory notice of deficiency, under I.R.C. §6212, which entitles the taxpayer to seek Tax Court review of a proposed tax deficiency. This is not a delinquent tax because it is not a final tax liability. Should the taxpayer seek Tax Court review, this will not be a final tax liability until the taxpayer has exercised all judicial appeal rights.

(ii) The IRS has filed a notice of Federal tax lien with respect to an assessed tax liability, and the taxpayer has been issued a notice under I.R.C. §6320 entitling the taxpayer to request a hearing with the IRS Office of Appeals contesting the lien filing, and to further appeal to the Tax Court if the IRS determines to sustain the lien filing. In the course of the hearing, the taxpayer is entitled to contest the underlying tax liability because the taxpayer has had no prior opportunity to contest the liability. This is not a delinquent tax because it is not a final tax liability. Should the taxpayer seek tax court review, this will not be a final tax liability until the taxpayer has exercised all judicial appeal rights.

(iii) The taxpayer has entered into an installment agreement pursuant to I.R.C. §6159. The taxpayer is making timely payments and is in full compliance with the agreement terms. The taxpayer is not delinquent because the taxpayer is not currently required to make full payment.

(iv) The taxpayer has filed for bankruptcy protection. The taxpayer is not delinquent because enforced collection action is stayed under 11 U.S.C. 362 (the Bankruptcy Code).

(ii) The Offeror has [[_] has not [_], within a three-year period preceding this offer, had one or more contracts terminated for default by any Federal agency.

(2) “Principal,” for the purposes of this certification, means an officer; director; owner; partner; or a person having primary management or supervisory responsibilities within a business entity (e.g., general manager; plant manager; head of a division or business segment; and similar positions).

This Certification Concerns a Matter Within the Jurisdiction of an Agency of the United States and the Making of a False, Fictitious, or Fraudulent Certification May Render the Maker Subject to Prosecution Under Section 1001, Title 18, United States Code.

(b) The Offeror shall provide immediate written notice to the Contracting Officer if, at any time prior to contract award, the Offeror learns that its certification was erroneous when submitted or has become erroneous by reason of changed circumstances.

(c) A certification that any of the items in paragraph (a) of this provision exists will not necessarily result in withholding of an award under this solicitation. However, the certification will be considered in connection with a determination of the Offeror’s responsibility. Failure of the Offeror to furnish a certification or provide such additional information as requested by the Contracting Officer may render the Offeror nonresponsible.

(d) Nothing contained in the foregoing shall be construed to require establishment of a system of records in order to render, in good faith, the certification required by paragraph (a) of this provision. The knowledge and information of an Offeror is not required to exceed that which is normally possessed by a prudent person in the ordinary course of business dealings.

(e) The certification in paragraph (a) of this provision is a material representation of fact upon which reliance was placed when making award. If it is later determined that the Offeror knowingly rendered an erroneous certification, in addition to other remedies available to the Government, the Contracting Officer may terminate the contract resulting from this solicitation for default.

(End of provision)

K.7 	52.209-13 VIOLATION OF ARMS CONTROL TREATIES OR AGREEMENTS – CERTIFICATION (JUN 2018)

(a) This provision does not apply to acquisitions below the simplified acquisition threshold or to acquisitions of commercial items as defined at FAR 2.101.

(b) Certification. [Offeror shall check either (1) or (2).]

________ (1) The Offeror certifies that—

(i) It does not engage and has not engaged in any activity that contributed to or was a significant factor in the President's or Secretary of State's determination that a foreign country is in violation of its obligations undertaken in any arms control, nonproliferation, or disarmament agreement to which the United States is a party, or is not adhering to its arms control, nonproliferation, or disarmament commitments in which the United States is a participating state. The determinations are described in the most recent unclassified annual report provided to Congress pursuant to section 403 of the Arms Control and Disarmament Act (22 U.S.C. 2593a). The report is available via the internet at https://www.state.gov/t/avc/rls/rpt/; and

(ii) No entity owned or controlled by the Offeror has engaged in any activity that contributed to or was a significant factor in the President's or Secretary of State's determination that a foreign country is in violation of its obligations undertaken in any arms control, nonproliferation, or disarmament agreement to which the United States is a party, or is not adhering to its arms control, nonproliferation, or disarmament commitments in which the United States is a participating state. The determinations are described in the most recent unclassified annual report provided to Congress pursuant to section 403 of the Arms Control and Disarmament Act (22 U.S.C. 2593a). The report is available via the internet at https://www.state.gov/t/avc/rls/rpt/; or

________ (2) The Offeror is providing separate information with its offer in accordance with paragraph (d)(2) of this provision.

(c) Procedures for reviewing the annual unclassified report (see paragraph (b)(1) of this provision). For clarity, references to the report in this section refer to the entirety of the annual unclassified report, including any separate reports that are incorporated by reference into the annual unclassified report.

(1) Check the table of contents of the annual unclassified report and the country section headings of the reports incorporated by reference to identify the foreign countries listed there. Determine whether the Offeror or any person owned or controlled by the Offeror may have engaged in any activity related to one or more of such foreign countries.

(2) If there may have been such activity, review all findings in the report associated with those foreign countries to determine whether or not each such foreign country was determined to be in violation of its obligations undertaken in an arms control, nonproliferation, or disarmament agreement to which the United States is a party, or to be not adhering to its arms control, nonproliferation, or disarmament commitments in which the United States is a participating state. For clarity, in the annual report an explicit certification of non-compliance is equivalent to a determination of violation. However, the following statements in the annual report are not equivalent to a determination of violation:

(i) An inability to certify compliance.

(ii) An inability to conclude compliance.

(iii) A statement about compliance concerns.

(3) If so, determine whether the Offeror or any person owned or controlled by the Offeror has engaged in any activity that contributed to or is a significant factor in the determination in the report that one or more of these foreign countries is in violation of its obligations undertaken in an arms control, nonproliferation, or disarmament agreement to which the United States is a party, or is not adhering to its arms control, nonproliferation, or disarmament commitments in which the United States is a participating state. Review the narrative for any such findings reflecting a determination of violation or non-adherence related to those foreign countries in the report, including the finding itself, and to the extent necessary, the conduct giving rise to the compliance or adherence concerns, the analysis of compliance or adherence concerns, and efforts to resolve compliance or adherence concerns.

(4) The Offeror may submit any questions with regard to this report by email to NDAA1290Cert@state.gov. To the extent feasible, the Department of State will respond to such email inquiries within 3 business days.

(d) Do not submit an offer unless—

(1) A certification is provided in paragraph (b)(1) of this provision and submitted with the offer; or

(2) In accordance with paragraph (b)(2) of this provision, the Offeror provides with its offer information that the President of the United States has—

(i) Waived application under U.S.C. 2593e(d) or (e); or

(ii) Determined under 22 U.S.C. 2593e(g)(2) that the entity has ceased all activities for which measures were imposed under 22 U.S.C.2593e(b).

(e) Remedies. The certification in paragraph (b)(1) of this provision is a material representation of fact upon which reliance was placed when making award. If it is later determined that the Offeror knowingly submitted a false certification, in addition to other remedies available to the Government, such as suspension or debarment, the Contracting Officer may terminate any contract resulting from the false certification.

(End of provision)

K.8	52.225-18    Place of Manufacture (Sept 2006)

(a) Definitions. As used in this clause—

“ Manufactured end product” means any end product in Federal Supply Classes (FSC) 1000-9999, except—

(1) FSC 5510, Lumber and Related Basic Wood Materials;

(2) Federal Supply Group (FSG) 87, Agricultural Supplies;

(3) FSG 88, Live Animals;

(4) FSG 89, Food and Related Consumables;

(5) FSC 9410, Crude Grades of Plant Materials;

(6) FSC 9430, Miscellaneous Crude Animal Products, Inedible;

(7) FSC 9440, Miscellaneous Crude Agricultural and Forestry Products;

(8) FSC 9610, Ores;

(9) FSC 9620, Minerals, Natural and Synthetic; and

(10) FSC 9630, Additive Metal Materials.

“Place of manufacture” means the place where an end product is assembled out of components, or otherwise made or processed from raw materials into the finished product that is to be provided to the Government. If a product is disassembled and reassembled, the place of reassembly is not the place of manufacture.

(b) For statistical purposes only, the offeror shall indicate whether the place of manufacture of the end products it expects to provide in response to this solicitation is predominantly—

(1)  [    ] In the United States (Check this box if the total anticipated price of offered end products manufactured in the United States exceeds the total anticipated price of offered end products manufactured outside the United States); or

(2)  [    ] Outside the United States.

K.9	AUTHORIZED CONTRACT ADMINISTRATOR

If the offeror does not fill-in the blanks below, the official who signed the offer will be deemed to be the offeror's representative for contract administration, which includes all matters pertaining to payments.

| Name: |  |
| --- | --- |
| Address: |  |
| Telephone No.: |  |

K.10	652.225-70    ARAB LEAGUE BOYCOTT OF ISRAEL (AUG 1999)

(a)  Definitions.  As used in this provision:

Foreign person means any person other than a United States person as defined below.

United States person means any United States resident or national (other than an individual resident outside the United States and employed by other than a United States person), any domestic concern (including any permanent domestic establishment of any foreign concern), and any foreign subsidiary or affiliate (including any permanent foreign establishment) of any domestic concern which is controlled in fact by such domestic concern, as provided under the Export Administration Act of 1979, as amended.

(b)  Certification.  By submitting this offer, the offeror certifies that it is not:

(1)  Taking or knowingly agreeing to take any action, with respect to the boycott of Israel by Arab League countries, which Section 8(a) of the Export Administration Act of 1979, as amended (50 U.S.C. 2407(a)) prohibits a United States person from taking; or,

(2)  Discriminating in the award of subcontracts on the basis of religion.

K.11  	RESERVED

K. 12      52.225-20     Prohibition on Conducting Restricted Business Operations in Sudan—Certification (AUG 2009)

(a) Definitions. As used in this provision—

“Business operations” means engaging in commerce in any form, including by acquiring, developing, maintaining, owning, selling, possessing, leasing, or operating equipment, facilities, personnel, products, services, personal property, real property, or any other apparatus of business or commerce.

“Marginalized populations of Sudan” means—

(1) Adversely affected groups in regions authorized to receive assistance under Section 8(c) of the Darfur Peace and Accountability Act (Pub. L. 109-344) (50 U.S.C. 1701 note); and

(2) Marginalized areas in Northern Sudan described in Section 4(9) of such Act.

“Restricted business operations” means business operations in Sudan that include power production activities, mineral extraction activities, oil-related activities, or the production of military equipment, as those terms are defined in the Sudan Accountability and Divestment Act of 2007 (Pub. L. 110-174). Restricted business operations do not include business operations that the person conducting the business can demonstrate—

(1) Are conducted under contract directly and exclusively with the regional government of southern Sudan;

(2) Are conducted pursuant to specific authorization from the Office of Foreign Assets Control in the Department of the Treasury, or are expressly exempted under Federal law from the requirement to be conducted under such authorization;

(3) Consist of providing goods or services to marginalized populations of Sudan;

(4) Consist of providing goods or services to an internationally recognized peacekeeping force or humanitarian organization;

(5) Consist of providing goods or services that are used only to promote health or education; or

(6) Have been voluntarily suspended.

(b) Certification. By submission of its offer, the offeror certifies that it does not conduct any restricted business operations in Sudan.

K.13.   52.209-2 Prohibition on Contracting with Inverted Domestic Corporations Representation (Nov 2015)

(a) Definitions. “Inverted domestic corporation” and “subsidiary” have the meaning given in the clause of this contract entitled Prohibition on Contracting with Inverted Domestic Corporations (52.209-10).

(b) Government agencies are not permitted to use appropriated (or otherwise made available) funds for contracts with either an inverted domestic corporation, or a subsidiary of an inverted domestic corporation, unless the exception at 9.108-2(b) applies or the requirement is waived in accordance with the procedures at 9.108-4.

(c) Representation. The Offeror represents that.

(1) It □ is, □ is not an inverted domestic corporation; and

(2) It □ is, □ is not a subsidiary of an inverted domestic corporation.

(End of provision)

SECTION L - INSTRUCTIONS, CONDITIONS, AND NOTICES TO OFFERORS

The Offeror shall include Defense Base Act (DBA) insurance premium costs covering their employees working on the contract to include American citizens, Individuals hired in the United States or its possessions, regardless of citizenship, Host Country Nationals (HCNs) and Third Country Nationals (TCNs) working overseas.  The offeror shall obtain DBA insurance directly from any Department of Labor approved providers at the DOL website at http://www.dol.gov/owcp/dlhwc/lscarrier.htm

L.1	52.252-1     SOLICITATION PROVISIONS INCORPORATED BY REFERENCE (FEB 1998)

This contract incorporates the following provisions by reference, with the same force and effect as if they were given in full text.  Upon request, the Contracting Officer will make their full text available.  The offeror is cautioned that the listed provisions may include blocks that must be completed by the offeror and submitted with its quotation or offer.  In lieu of submitting the full text of those provisions, the offeror may identify the provision by paragraph identifier and provide the appropriate information with its quotation or offer.

Also, the full text of a solicitation provision may be accessed electronically at:  http://acquisition.gov/far/index.html or http://farsite.hill.af.mil/vffara.htm.  Please note these addresses are subject to change.

If the Federal Acquisition Regulation (FAR) is not available at the locations indicated above, use an Internet “search engine” (for example, Google, Yahoo or Excite) to obtain the latest location of the most current FAR.

The following Federal Acquisition Regulation provisions are incorporated by reference (48 CFR CH. 1):

PROVISION		TITLE AND DATE

52.204-7 	SYSTEM FOR AWARD MANAGEMENT (OCT 2016)

52.204-16 		Commercial and Government Entity Code 	Reporting (JUL 2016)

52.209-7        	INFORMATION REGARDING RESPONSIBILITY MATTERS

(JULY 2013)

52.214-34		SUBMISSION OF OFFERS IN ENGLISH LANGUAGE (APR 	1991)

52.215-1		INSTRUCTIONS TO OFFERORS— COMPETITIVE 					ACQUISITION (JAN 2004)

### 52.222-56		CERTIFICATION REGARDING TRAFFICKING IN PERSONS

### (MAR 2015)

52.236-28		PREPARATION OF PROPOSALS - CONSTRUCTION

(OCT 1997)

L.2	SOLICITATION PROVISIONS IN FULL TEXT

52.216-1     TYPE OF CONTRACT (APR 1984)

The Government contemplates award of an indefinite-delivery indefinite-quantity contract resulting from this solicitation.

(End of provision)

52.233-2  SERVICE OF PROTEST (AUG 1996)

(a)	Protests, as defined in Section 33.101 of the Federal Acquisition Regulation, that are filed directly with an agency, and copies of any protests that are filed with the General Accounting Office (GAO), shall be served on the Contracting Officer (addressed as follows) by obtaining written and dated acknowledgment of receipt from U.S. Embassy Lusaka, Subdivision 694 Lot 100 Ibex Hill Road Lusaka, Zambia.

(b)	The copy of any protest shall be received in the office designated above within one day of filing a protest with the GAO.

(End of provision)

L.3	REVIEW OF DOCUMENTS

Each Offeror is responsible for:

- Obtaining a complete set of contract drawings and specifications;

- Thoroughly reviewing such documents and understanding their requirements;

- Visiting the project site and becoming familiar with all working conditions, local laws and regulations; and

- Determining that all materials, equipment and labor required for the work are available.

Offerors shall report any ambiguity in the solicitation, including specifications and contract drawings immediately to the Contracting Officer.  Any prospective Offeror who requires a clarification, explanation or interpretation of the contract requirements shall make a request to the Contracting Officer not less than five working days before the closing date of the solicitation. Offerors may rely ONLY on written interpretations by the Contracting Officer.

L.4	SUBMISSION OF OFFERS

L.4.1	GENERAL

This solicitation is for the performance of the construction services described in Section C - DESCRIPTION/SPECIFICATIONS/WORK STATEMENT, and the Attachments and Exhibits that are a part of this solicitation.

L.4.2	SUMMARY OF INSTRUCTIONS

Each offer must consist of the following physically separate volumes:

Volume	Title							No. of Copies*

### 1		Executed Standard Form 1442, "Solicitation,		____3___

Offer and Award (Construction, Alteration,

or Repair)", and completed Section K -

REPRESENTATIONS, CERTIFICATIONS AND OTHER

STATEMENTS OF OFFERORS.

2		Price Proposal and completed Section B - 		___3____

SUPPLIES OR SERVICES AND PRICES/COSTS.

The price proposal shall include a completed

Section J, Exhibit 9, "BREAKDOWN OF

PROPOSAL PRICE BY DIVISIONS OF SPECIFICATIONS.”

3		Business Management/Technical Proposal.		____3____

Submit the complete offer to the address indicated at Block 7 of Standard Form (SF) 1442, if mailed, or the address below, if hand delivered (if this is left blank, the address is the same as that in Block 7 of SF-1442).

Offerors shall identify, explain and justify any deviations, exceptions, or conditional assumptions taken regarding any of the instructions or requirements of this solicitation.

*The total number of copies includes the original as one of the copies.

L.4.3	DETAILED INSTRUCTIONS

L.4.3.1	  Volume I:  Standard Form (SF) 1442 and Section K. Complete Blocks 14 through 20C of the SF-1442 and all of Section K.

L.4.3.2   Volume II:  Price proposal and Section B.  The price proposal shall consist of completion of Section B and Section J, Attachment 4, "BREAKDOWN OF PROPOSAL PRICE BY DIVISIONS OF SPECIFICATIONS.  All applicable portions of this form shall be completed in each relevant category (such as labor, materials, etc.).

L.4.3.3	  Volume III:  Business Management/Technical Proposal.

(a)  Present the performance schedule in the form of a bar chart indicating when the various portions of the work will be started and completed within the required schedule.  This bar chart shall be in sufficient detail to clearly show each segregable portion of work and its planned start and completion date.

(b)  The Business Management/Technical Proposal shall be in two parts, including the following information:

Proposed Work Information - Provide the following:

- A list of the names, addresses and telephone numbers of the owners, partners, and principal officers of the Offeror;

- The name and address of the Offeror's field superintendent for this project; and

- A list of the names, addresses, and telephone numbers of subcontractors and principal materials suppliers to be used on the project, indicating what portions of the work will be performed by them.

- Proof of registration for National Council for Construction, minimum grade 5.

- Copies of advanced certification in Building Construction for the Foreman

- Letters of credit from the bank or proof of liquid capital

- Proof of registration to the Engineering Institute of Zambia (EIZ)

- Proof of subscribing to Workers Compensation in lieu of insurance

Experience and Past Performance - List all contracts and subcontracts your company has held over the past three years for the same or similar work.  Provide the following information for each contract and subcontract:

- Customer's name, address, and telephone numbers of customer's lead contract and technical personnel;

- Contract number and type;

- Date of the contract award place(s) of performance, and completion dates;

- Contract dollar value;

- Brief description of the work, including responsibilities;

- Comparability to the work under this solicitation;

- Brief discussion of any major technical problems and their resolution;

- Method of acquisition (fully competitive, partially competitive, or noncompetitive), and the basis for award (cost/price, technical merit, etc.);

- Cost/price management history, including any cost overruns and under runs, and cost growth and changes;

- Percent turnover of contract key technical personnel per year; and

- Any terminations (partial or complete) and the reason (convenience or default).

(12)	 Environmental Preferability Submission, describing how the offeror will ensure the use of environmentally friendly products and materials in the performance of the contract.  The offeror must list all chemical cleaning products and non-chemical products that will be used.

L.5	52.236-27    SITE VISIT (FEB 1995)

(a)  The clauses at 52.236-2, Differing Site Conditions, and 52.236-3, Site Investigations and Conditions Affecting the Work, will be included in any contract awarded as a result of this solicitation.  Accordingly, offerors or quoters are urged and expected to inspect the site where the work will be performed.

(b)  An organized site visit has been schedule for Thursday December 6th, 2018 at 09:30am Local time.

(c)  Participants will meet at 20A Off Mutende Road.

L.6	PREPROPOSAL CONFERENCE

A pre-proposal conference to discuss the requirements of this solicitation will be held on Thursday 6th, December, 2018 at 09:30am Local time at 20A Off Mutende Road.  Offerors are urged to submit written questions using the address provided on the solicitation cover page of this solicitation.  Attendees should bring written questions to the conference as well.  As time permits and after the Embassy discusses the solicitation and written questions are answered, oral questions may be taken.

L.7	652.206-70 ADVOCATE FOR COMPETITION/OMBUDSMAN (FEB 2015)

(a) The Department of State’s Advocate for Competition is responsible for assisting industry in removing restrictive requirements from Department of State solicitations and removing barriers to full and open competition and use of commercial items. If such a solicitation is considered competitively restrictive or does not appear properly conducive to competition and commercial practices, potential offerors are encouraged first to contact the contracting office for the solicitation. If concerns remain unresolved, contact:

- For solicitations issued by the Office of Acquisition Management (A/LM/AQM) or a Regional Procurement Support Office, the A/LM/AQM Advocate for Competition, at AQMCompetitionAdvocate@state.gov.

- For all others, the Department of State Advocate for Competition at cat@state.gov.

(b) The Department of State’s Acquisition Ombudsman has been appointed to hear concerns from potential offerors and contractors during the pre-award and post-award phases of this acquisition. The role of the ombudsman is not to diminish the authority of the contracting officer, the Technical Evaluation Panel or Source Evaluation Board, or the selection official. The purpose of the ombudsman is to facilitate the communication of concerns, issues, disagreements, and recommendations of interested parties to the appropriate Government personnel, and work to resolve them. When requested and appropriate, the ombudsman will maintain strict confidentiality as to the source of the concern. The ombudsman does not participate in the evaluation of proposals, the source selection process, or the adjudication of formal contract disputes. Interested parties are invited to contact the contracting activity ombudsman, The Management Officer, at 0026-0211357000. For an American Embassy or overseas post, refer to the numbers below for the Department Acquisition Ombudsman. Concerns, issues, disagreements, and recommendations which cannot be resolved at a contracting activity level may be referred to the Department of State Acquisition Ombudsman at (703) 516-1696 or write to: Department of State, Acquisition Ombudsman, Office of the Procurement Executive (A/OPE), Suite 1060, SA-15, Washington, DC 20520.

(End of provision)

L.8	MAGNITUDE OF CONSTRUCTION PROJECT

It is anticipated that the range in price of this contract will be: Between $1,000,000.00 and $5,000,000.00.

L.9	FINANCIAL STATEMENT

If asked by the Contracting Officer, the offeror shall provide a current statement of its financial condition, certified by a third party that includes:

Income (profit-loss) Statement that shows profitability for the past 3 years;

Balance Sheet that shows the assets owned and the claims against those assets, or what a firm owns and what it owes; and

Cash Flow Statement that shows the firm’s sources and uses of cash during the most recent accounting period.  This will help the Government assess a firm’s ability to pay its obligations.

The Government will use this information to determine the offeror’s financial responsibility and ability to perform under the contract.  Failure of an offeror to comply with a request for this information may cause the Government to determine the offeror to be nonresponsible.

SECTION M - EVALUATION FACTORS FOR AWARD

M.1	EVALUATION OF PROPOSALS

M.1.1.	 General.  To be acceptable and eligible for evaluation, proposals must be prepared following Section L and must meet all the requirements in the other sections of this solicitation.

M.1.2.	BASIS FOR AWARD

The Government intends to award a contract resulting from this solicitation to the lowest priced, technically acceptable offeror who is a responsible contractor.  The evaluation process will follow the procedures below:

- Initial Evaluation

The Government will evaluate all proposals received will be evaluated to ensure that each proposal is complete in terms of submission of each required volume, as specified in Section L.  The Government may eliminate proposals that are missing a significant amount of the required.

- Technical Acceptability

After the initial evaluation, the Government will review the remaining proposals to determine technical acceptability.  Technical acceptability will include a review of the Proposed Work Information described in Section L to ensure that the offeror's proposed project superintendent and subcontractors are acceptable to the Government.  The Government may also contact references provided as part of the Experience and Past Performance information described in Section L to verify quality of past performance.  The Government shall also review the bar chart submitted to review the sequence of work and to ensure that performance would be completed on time.  The end result of this review will be a determination of technical acceptability or unacceptability.

(c)  The Government will determine responsibility by analyzing whether the apparent successful offeror complies with the requirements of FAR 9.1, including:

- Adequate financial resources or the ability to obtain them;

- Ability to comply with the required performance period, taking into consideration all existing commercial and governmental business commitments;

- Satisfactory record of integrity and business ethics;

- Necessary organization, experience, and skills or the ability to obtain them;

- Necessary equipment and facilities or the ability to obtain them; and

- Otherwise qualified and eligible to receive an award under applicable laws and regulations.

The Government reserves the right to reject proposals that are unreasonably low or high in price. Unsuccessful offerors will be notified in accordance with FAR 15.503.

M.1.3	AWARD SELECTION

The Government will review the prices of all technically acceptable firms and the award selection will go to the lowest priced, technically acceptable, responsible offeror.  As described in FAR 52.215-1, incorporated by reference in Section L, the Government may award may based on initial offers, without discussions.

M.1.4      52.216-27 SINGLE OR MULTIPLE AWARDS (OCT 1995)

The Government may elect to award a single task order contract or to award multiple delivery order contracts or task order contracts for the same or similar supplies or services to two or more sources under this solicitation.

M.2	52.217-5    EVALUATION OF OPTIONS (JULY 1990)

The Government will evaluate offers for award purposes by adding the total price for all options to the total price.  Evaluation of options will not obligate the Government to exercise the option(s).

(End of provision)

M.3	QUANTITIES FOR EVALUATION

For the purpose of evaluation, and for no other purpose, evaluation of prices submitted will be made on the basis that the Government will require the quantities shown in Section B of this solicitation.

M.4	SEPARATE CHARGES

Separate charges, in any form, are not solicited.  For example, proposals containing any charges for failure of the Government to exercise any options will be rejected.  The Government shall not be obligated to pay any charges other than the contract price, including any exercised options.

M.5	52.225-17   EVALUATION OF FOREIGN CURRENCY OFFERS (FEB 2000)

If the Government receives offers in more than one currency, the Government will evaluate offers by converting the foreign currency to United States currency using the exchange rate used by the Embassy in effect as follows:

(a)  For acquisitions conducted using sealed bidding procedures, on the date of bid 	opening.

(b)  For acquisitions conducted using negotiation procedures—

- On the date specified for receipt of offers, if award is based on initial offers; otherwise

- On the date specified for receipt of proposal revisions.

(End of provision)