ITEM NO 1    	HAND SINK

Quantity Req'd.: 	1

Manufacturer: 	Eagle

Model No.:       	HSAN-10-F

Status:          	In Contract

Hand Sink.

- MicroGard antimicrobial protection.

- T&S faucet with wrist handles in lieu of standard faucet.

- End splash both ends.

- Wall mount soap and towel dispenser by owner

ITEM NO 2    	SLICER

Quantity Req'd.: 	1

Manufacturer: 	Hobart Corp.

Model No.:       	2612

Status:          	In Contract

Slicer, Food, manual feed, 12" diameter knife, cast aluminum base, belt-driven blade assembly.

- 4" legs.

ITEM NO 3    	MICROWAVE OVEN

Quantity Req'd.: 	1

Manufacturer: 	Sharp Elec

Model No.:       	R-23GTF

Status:          	In Contract

Microwave Oven to be located on lower shelf of Item 6.

- Provide with cord and plug

- Provide with manufacturer’s standard specifications

ITEM NO 4    	BASIC TABLE

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be size and shape as shown on plan x 36" high per detail C-7-1, w/ 6" high splash per detail C-1-1B and Type "A" edge per detail C-1-1A. Provide with the following:

- One (1) 20" x 20" x 5" deep drawer per detail C-1-3A, C-1-3C and C-1-3D, locking hasp.

- Under shelf per C-7-1.

- 6” high Backsplash at rear and left end with closed back.

ITEM NO 5    	MIXER, 20-QUART

Quantity Req'd.: 	1

Manufacturer: 	Hobart Corp.

Model No.:       	HL200

Status:          	In Contract

Standard accessory package.

ITEM NO 6    	WALL SHELF

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be of size and shape as shown on plan per detail C-1-2 with the following requirements:

- Two-tier unit, first tier (lower shelf) to be 12" wide with accommodation for microwave oven, item 3, second tier (upper) to be 15" wide and extend to wall above item 4 basic table as per plan.

ITEM NO 7    	PREP TABLE W/2-SINKS

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be size and shape as shown on plan x 36" high per detail C-7-1B  w/ 6" high splash per detail C-1-1B Type "V" inverted edge per detail C-1-1A.  Provide with the following:

- 2 (Two) 20" x 20" x 12" deep sink w/ Type 3 faucet.

- Undershelf per C-7-1.

- One (1) 20" x 20" x 5" deep drawer per detail C-1-3A, C-1-3C and C-1-3D, locking hasp.

- 6” high back splash

- Left end splash with “closed back” as per plan

- Rotary waste with lever

ITEM NO 8    	FREEZER, 2-SECTION

Quantity Req'd.: 	1

Manufacturer: 	Traulsen Co.

Model No.:       	ALT232NUT-FHS

Status:          	In Contract

Freezer, Reach-in, Two-Section, Self-Contained Refrig System, aluminum interior, stainless exterior, standard depth cabinet, narrow full-height doors, with exterior digital thermometer.

- 6” polyurethane swivel casters with two locking brakes on front

- 6’ cord and plug, attached

- Field reversible doors hinged as shown on plan

- Full complement of Universal type tray slides 4” O.C. (credit for chrome plated shelves)

- Doors w/ cylinder locks common keyed

- Chrome plated pad lock hasp

- 5 year compressor warranty

- Two year service/labor warranty

ITEM NO 9    	WALK-IN COOLER

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	Custom

Status:          	In Contract

Refrigerated Storage Unit +35º F, Walk-in, for installation on concrete slab, of size and shape as shown on plan x 9’-2.25” overall height (nominal). 4” urethane wall and ceiling panels, U.L. Flame Spread 25 insulation. Panels without wooden structural members. Hinged entrance doors to be flush type, hinged as shown on plan. Thru ceiling door electrical assembly as shown on detail E-1-4

- Align height inside walk in with finished floor height out side of walk in for smooth uninterrupted transition

- Floorless with flat bottom wall panels with 4” metal screed.  Floor finish to match kitchen floor

- 1 Lot Closure panels per detail CSR-2-1 with finish to match exposed wall finish (F.S.E.C.) to verify finished ceiling height

- 1 Lot trim strip where required to close wall gaps with finish to match that of exposed wall panels to from floor to ceiling (F.S.E.C.) to verify finished ceiling height

- 36”x84” door with third hinge

- diamond plate wainscot on all exposed surfaces 36” high

- bumper rail at 36”

- 14x14” viewport

- Stucco aluminum interior and exposed exterior

- Unexposed exterior to be galvalume

- Kason Dead bolt lock. Automatic door close, Kason K-194

- Approved Lithonia light fixtures and switches per detail E-1-4, installed and wired by electrical division. (See electrical plan for quantity and location of lights and switches)

- Modularm 75B, recessed with thru ceiling door electrical as shown on detail E-1-4

- Diamond Tread kick plate 36” high on interior and exterior door

ITEM NO 10    	SHELVING

Quantity Req'd.: 	LOT

Manufacturer: 	Metro Equipment Corporation,

Model No.:       	METROMAX  Q

Status:          	In Contract

Of size and shape as shown on plan x 5 tiers high.  74" high posts to match shelf type. 5" diameter polyurethane swivel casters, two (2) with brakes.

ITEM NO 11    	DUNNAGE RACK

Quantity Req'd.: 	LOT

Manufacturer: 	Metro Equipment Corporation,

Model No.:       	METRO BOW TIE DUNNAGE RACKS

Status:          	In Contract

Of size and shape as shown on plan.

ITEM NO 12    	EVAPORATOR COIL, MEDIUM TEMPERATURE

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	AM-104

Status:          	In Contract

Unit to be adequately sized to operate Item 9, Refrigerator Compartment @ +35° F.  Electrical hook-up and interconnecting of system to be by the Electrical Contractor.

ITEM NO 13    	CONDENSING UNIT, AIR COOLED

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	PR154M

Status:          	In Contract

F.S.E.C. to provide the necessary refrigeration lines required to operate and maintain the refrigeration system for Item 9, refrigerated compartment.  Unit to be part of the remote refrigeration system for Item 12, Evaporator Coil.

F.S.E.C. to coordinate with the electrical/plumbing contractor to provide a complete and operable refrigeration system.

Provide start-up, five (5) year compressor warranty and one (1) year refrigeration service contract.

Division 16 to wire to safety disconnect switch.

- Unit to be located in janitor closet unless other wise specified by architect.  See Architectural plan for location.

- Assume a 50' refrigeration line run

- Protective cover for "inside" application.

ITEM NO 14    	CAN STORAGE RACK

Quantity Req'd.: 	1

Manufacturer: 	New Age

Model No.:       	1250

Status:          	In Contract

Can Storage Rack.

- Lifetime warranty.

- Shelf insert for smaller than NO. 5 cans (1255)

- Caster lock for 5" platform caster (C495 & C500).

ITEM NO 15    	TRASH RECEPTACLE (44 GAL.) (NIC)

Quantity Req'd.: 	1

Manufacturer: 	Rubbermaid

Model No.:       	2643-06

Status:          	By Owner/Operator

This item is not in contract. The specification is for reference only. The item is shown on the drawing for informational purposes and generally represents the size/ capacity of unit to be provided by the Owner.

ITEM NO 16    	FIRE SUPPRESSION SYSTEM

Quantity Req'd.: 	1

Manufacturer: 	Ansul

Model No.:       	R-102

Status:          	In Contract

Fire protection system to be provided and installed by FSE Contractor per detail C-22-6 and C-22-7. System to be Ansul R102 system, wet chemical, mount tight to underside of finished ceiling, provide with the following specifications:

- Wet chemical suppressant.

- System U.L. Listed, installed in accordance with manufacturer's recommendations, and comply with NFPA 13 and local codes.

- System to be pre-piped and fusible link detection incorporated with ventilator sections by ventilator manufacturer at time of construction.

- Wherever possible, system piping shall be unexposed. Exposed piping, conduit and nozzles shall be smooth chrome-plated or stainless steel.

- Fusible link assemblies shall be unexposed within the ventilator bodies or within enclosed boxes recessed into ventilator roof.

- System shall be shipped complete with tanks, automan release, remote manual release.

- Cylinders and controls shall be mounted on wall where shown on plan at an accessible height that will not conflict with equipment below.

- Mechanically activated gas shut off valves are to be furnished by the FSE Contractor and installed by the Plumbing Contractor.

- Coordination and cabling to valve by FSE Contractor.

- Shunt trip type breaker disconnect provided and installed by the Electrical Division.

- FSEContractor to coordinate shunt trip breaker requirements with the Electrical Contractor.

- System to provide plenum and duct collar protection and surface protection for equipment underneath Item 30, Exhaust Hood.

- FSE Contractor will be required to obtain all permits and arrange for system inspection and testing to achieve an approved operating system.

Remote pull station:

- Fire Protection System remote manual activation stations are to be flush wall-mounted, with the cabling conduit recessed within the wall.

- Remote pull stations are to be located along pathways between the protected equipment and area exits, and in accord with any governing local code requirements.  FSE Contractor to confirm placement of remote fire pulls w/ Fire Suppression System Subcontractor and reflect code compliant placement on dimensioned rough-in plans.

- FSE Contractor shall coordinate the efforts between the Fire Protection System subcontractor, any other trades, and with local code enforcement officials, as may be necessary to comply with local codes.

- If the FSE contractor determines that, for any reason, the flush mounting of the remote fire pulls is not possible an appropriate and timely “Inability to Comply” statement must be furnished to CFL for their review and response.

ITEM NO 17    	MOBILE TABLE W/ SHELVES

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be size and shape as shown on plan x 36" high per detail C-7-1 w/ 6" high splash per detail C-1-1B “closed back”. Type "A" edge per detail C-1-1A.  Provide with the following:

- One (1) 20" x 20" x 5" deep drawer per detail C-1-3A, C-1-3C and C-1-3D, locking hasp.

- Under shelf per C-7-1.

- 5" diameter polyurethane swivel casters.

- Shelf, splash mounted, two tiers of size and shape as shown on plan per Detail C-1-6. FSEC to coordinate shelf height with Ansul System above.

ITEM NO 18    	UTILITY RACK

Quantity Req'd.: 	2

Manufacturer: 	Cres Cor  (200 Series)

Model No.:       	210-1841A

Status:          	In Contract

Rack, Mobile Utility, full height, open sides, with slides for 18"x26" trays, slides on approximately 3" centers, welded tubular aluminum frame.

- Floor lock

- 5" polyurethane casters.

- Corner bumpers

ITEM NO 19    	REFRIGERATOR, 2-SECTION

Quantity Req'd.: 	1

Manufacturer: 	Traulsen Co.

Model No.:       	AHT232NUT-FHS

Status:          	In Contract

Refrigerator, Reach-in, Two-Section, Self-Contained Refrigeration System, aluminum interior, stainless steel exterior, standard depth cabinet, narrow full-height doors, with exterior digital thermometer.

- 6” polyurethane swivel casters with two locking brakes on front

- 6’ cord and plug

- Field reversible doors hinged as shown on plan

- Full compliment of Universal type tray slides 4” O.C. (credit for chrome plated shelves)

- Doors w/ cylinder locks common keyed

- Chrome plated pad lock hasp

- 5 year compressor warranty

- Two year service/labor warranty

ITEM NO 20    	SHELVING

Quantity Req'd.: 	LOT

Manufacturer: 	Metro Equipment Corporation,

Model No.:       	SUPER ERECTA

Status:          	In Contract

Of size and shape as shown on plan stainless steel finish x 5 tiers high.  86" high posts to match shelf type. Furnish with set of four (4) polyurethane casters, two with brakes.

ITEM NO 21    	PASS THRU WINDOW

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Pass Thru Window of size and shape as shown on plan @ 35" -AFF per detail C-8-15

- Window opening to be 18" tall x 30" wide

ITEM NO 22    	PASS THRU WINDOW W/ ROLL DOWN GATE (NIC)

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	Specified By Architect/Interior Designer

Pass Thru Window W/ roll Down Gate with Roll Down Shutter with removable hinged locking closure panel

- This item is not in contract. It is specified by the Architect.

ITEM NO 23    	WALL SHELF, TWO TIER

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be of size and shape as shown on plan per detail C-1-2 with the following requirements:

- Louvers per detail C-1-2.

- Two-tier unit, first tier (lower shelf) to be 12" wide, second tier (upper) to be 15" wide.

ITEM NO 24    	POT SINK, THREE COMPARTMENT

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be of size and shape as shown on plan x 34" high to drain board level with 10" high splash per details C-1-1A Type "D" edge, C-1-1B backsplash, C-8-1 and C-8-5.  End splashes as shown on plan. (3) sinks - wash 30"x24", rinse 24"x24", sanitize 24"x24", all 14" deep with the following requirements:

- Overflow collector per detail C-8-8.

- Under shelf below right and left drain board section per detail C-8-1.

- Front to back and rear cross rails at section of pass thru window to accommodate trash can below counter

- 2 Type 3 faucet(s).

- Rotary Drain with lever waste

- 10” back splash as per plan provide notched opening in backsplash at pass through window as per detail C-8-15

ITEM NO 25    	TABLE

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Unit to be size and shape as shown on plan x 36" high per detail C-7-1 w/ 6" high splash per detail C-1-1B Type "A" edge per detail C-1-1A.  Provide with the following:

- Open base table with rear and side cross bar

ITEM NO 26    	6 BURNER RANGE W/ 24" GRIDDLE

Quantity Req'd.: 	1

Manufacturer: 	Garland Ind

Model No.:       	S284

Status:          	In Contract

Range, 60" Restaurant, Gas-Fired, two standard ovens, stainless steel front and sides, stainless steel backsplash/flue riser.

- Natural gas

- Flexible gas hose w/quick disconnect & restraining device

- 5/8” heavy duty griddle plate 24” wide

- Stainless Steel back guard and double shelf.

- 6” polyurethane swivel casters with two locking front brakes

ITEM NO 27    	DOUBLE CONVECTION OVEN, GAS

Quantity Req'd.: 	1

Manufacturer: 	Blodgett Co.

Model No.:       	DFG100 DOUBLE

Status:          	In Contract

Natural gas convection oven with Manual Controls.  Provide with the following

- 4.25" low profile casters (double only)

- Gas presser regulator, flexible gas hose w/quick disconnect & restraining device

- Interior liner stainless steel(per section)

- Stainless steel door with view panel.

- Gas manifold

- Flue connector

ITEM NO 28    	HOLDING CABINET, FULL HEIGHT

Quantity Req'd.: 	1

Manufacturer: 	Winston

Model No.:       	HA4022-HR-3

Status:          	In Contract

Holding Cabinet, Full Height. .

- Without windows.

- Wire rack (4 pack).

- Full perimeter bumpers w/ 5" casters.

- Extended warranty.

- Scale Kleen Packets (12 pack)

- Doors hinged per plan

ITEM NO 29    	HAND SINK

Quantity Req'd.: 	1

Manufacturer: 	Eagle

Model No.:       	HSAN-FS

Status:          	In Contract

Hand Sink.

- MicroGard antimicrobial protection.

- T&S faucet with wrist handles in lieu of standard faucet.

- Provide hose bibb assembly mounted below sink

- Wall mounted soap and towel dispense by owner

ITEM NO 30    	EXHAUST HOOD, WALL MOUNTED

Quantity Req'd.: 	1

Manufacturer: 	Gaylord, Inc.

Model No.:       	GX2-BDL-CA-60

Status:          	In Contract

Unit to be U.L. listed grease extractor, high velocity wall mounted canopy of size and shape as shown on plan 24" high, built in 1 section and mounted 6'-8" AFF. One (1) lot stainless steel enclosure paneling, at all open sides, to finished ceiling (F.S.E. Contractor to verify height). Paneling must be supplied by Exhaust Hood Manufacturer and installed by F.S.E. Contractor. Adhere to Specific Conditions for installation of fabricated equipment. Ventilator to be U.L. and NSF listed and be in full accordance with NFPA 96 and all state/local codes/ordinances applicable. F.S.E. Contractor to supply the necessary mounting rods for hanging ventilator. Exhaust air requirements as shown on plans.

Options:

- Recessed incandescent light fixtures as indicated on electrical plan.

- Ventilator shall be equipped with a full length fire damper located in the ventilator extractor plenum between the extractor inserts and the ventilator duct collar.  Exhaust fire dampers located at the duct collar are not acceptable. The damper shall be controlled by an electrically driven actuator, specifically listed for such use and shall be activated by fail safe thermostat(s) located at the duct collar.  The damper shall also close each time the exhaust fan is turned off, to prevent conditioned air from escaping the occupied space via thermal drafts, and then re-open when the exhaust fan is started.

- Pre-piping of the Item 16, Fire Suppression System is to be provided by the Exhaust Hood manufacturer at the time of hood fabrication.

- Pre-piping to include fusible-link detector bracket assemblies and cable runs, and wet-chemical manifold piping, duct collar and plenum protection piping with termination nozzles, and cooking appliance nozzle drops with termination nozzles.

- Location of cooking appliance nozzle drops are to be fully dimensioned on hood submission drawings.

- Fusible link detector and wet chemical piping terminations to be coordinated with the FSE Contractor and clearly indicated on hood submission drawings.

- Access to the fusible links for inspection and change-outs to be provided.  The hood manufacturer and FSE Contractor to coordinate their efforts to assure the necessary access.

FSE Contractor is responsible for fit of equipment. Prior to releasing hoods for fabrication, FSE Contractor needs to verify field conditions (existing &/or proposed) and to determine clearances to all structural items, obstructions, etc. The FSE Contractor will coordinate with other trades to confirm that the hood can be mounted as proposed and that the ductwork and final connection can be accommodated without conflict.  Failure to perform this step may result in modifications to the exhaust hood at the FSE Contractor's expense.

ITEM NO 31    	PASS-THRU REFRIGERATOR, 1 SECTION

Quantity Req'd.: 	1

Manufacturer: 	Traulsen Co.

Model No.:       	AHT132WPUT-FHS

Status:          	In Contract

Refrigerator, Reach-Thru, One-Section, Self-Contained Refrig System, aluminum interior, stainless steel exterior, standard depth cabinet, wide full-height doors, with exterior digital thermometer.

- 6’ cord and plug

- Field reversible doors hinged as per plan

- Full compliment of Universal tray slides 4” O.C. (credit for chrome plated shelves)

- 6” casters with two locking front brakes

- Doors w/ cylinder locks common keyed

- Chrome plated pad lock hasp

- 5 year compressor warranty

- Two year service/labor warranty

- Stainless steel shelves in lieu of chrome plated

ITEM NO 32    	PASS THRU HEATED CABINET, 1-SECTION

Quantity Req'd.: 	1

Manufacturer: 	Traulsen Co.

Model No.:       	AHF132WP-FHS

Status:          	In Contract

Heated Cabinet, Reach-Thru, One-Section, aluminum interior, stainless exterior, standard depth cabinet, wide doors, with exterior dial-type thermometer.

- 6’ cord and plug

- Field reversible doors hinged as per plan

- Full compliment of Universal tray slides 4” O.C. (credit for chrome plated shelves)

- 6” casters with two locking front brakes

- Doors w/ cylinder locks common keyed

- Chrome plated pad lock hasp

- Two year service/labor warranty

- Stainless steel shelves in lieu of chrome plated

ITEM NO 33    	WORK TABLE W/ UTILITLY SINK

Quantity Req'd.: 	1

Manufacturer: 	Custom Fabricated Assembly

Status:          	In Contract

Counter, open front cabinet base stainless steel top and base, Unit to be of size and shape as shown on plan x 36” high per detail C-2-1 and C-7-1B w/ 6” splash per detail C-1-1B Type “V”  inverted edge, per detail C-1-1A. End splashes as shown on plan.  Provide with the following:

- Backsplash as shown on plan per detail C-1-1B. Return end splashes as shown on plan, finished back when exposed similar to detail C-1-1B “closed back."

- Notch at pass through window where shown on plan and extend stainless ledge over wall opening with front bullnose edge.

- 16" x 20" x 12" deep sink w/ Type3 faucet.

- Open storage with one adjustable intermediate shelf to left of sink and right of drawers per detail C-2-1

- Three (3) 20" x 20" x 5" deep drawers stacked per detail C-1-3A, C-1-3B, C-1-3C and C-1-3D, locking hasp

- 6” legs below counter section

- Sink cover per detail C-8-17

- Front  to back and rear cross rails below sink section per detail C-7-1B

ITEM NO 34    	PASS-THRU REFRIGERATOR, 1-SECTION

Quantity Req'd.: 	1

Manufacturer: 	Traulsen Co.

Model No.:       	AHT132WPUT-FHS

Status:          	In Contract

Refrigerator, Reach-Thru, One-Section, Self-Contained Refrig System, aluminum interior, stainless steel exterior, standard depth cabinet, wide full-height doors, with exterior digital thermometer.

- 6’ cord and plug

- Field reversible doors hinged as per plan

- Full Compliment of Universal tray slides 4” O.C. (credit for chrome plated shelves)

- 6” casters with two locking front brakes

- Doors w/ cylinder locks common keyed

- Chrome plated pad lock hasp

- 5 year compressor warranty

- Two year service/labor warranty

- Stainless steel shelves in lieu of chrome plated

ITEM NO 35    	HAND SINK

Quantity Req'd.: 	1

Manufacturer: 	Eagle

Model No.:       	HSAN-10-F

Status:          	In Contract

Hand Sink.

- MicroGard antimicrobial protection.

- T&S faucet with wrist handles in lieu of standard faucet.

- End splash left end.

- Skirt assembly

- Wall mounted soap and towel dispenser by owner

ITEM NO 36    	MILK CABINET, REFRIGERATED

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	KBFD-8

Status:          	In Contract

Milk Dispenser w/ 8 crate capacity

- Lid locks

- 5" casters concealed within body

- 6’ cord and plug

- Padlock hasp

- Corner bumpers

- 5 year compressor warranty

- Extended parts and labor warranty

- Fiberglas body panels Color to be determined by architect

ITEM NO 37    	COLD SERVING UNIT, MOBILE

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	K60-CFMA

Status:          	In Contract

Serving Counter, Cold Food, Cafeteria, mobile modular design, single sided,  open base with apron, stainless steel top, refrigerated cold pan, 4-pan size, stainless steel base. Factory wire lights and controls to single cord and plug.

- Chamfered continuous solid stainless top with integral tray slide with mitered edges at 30” AFF.

- unit to be 30" high to top of tray slide

- Line up locks

- 5” swivel caster

- breath shield, single service

- 6’ cord and plug

- Open base design at rear with adjustable intermediate shelf

- Fluorescent Lights

- Adapter bars for cold pan

- 5 year compressor warranty

- Extended parts and labor warranty

- Locate drain on side closest to hot food table

- Vent compressor through louvered panel on kitchen side

ITEM NO 38    	HOT FOOD COUNTER, MOBILE

Quantity Req'd.: 	1

Manufacturer: 	Colorpoint

Model No.:       	KEF6-CPA-MOD

Status:          	In Contract

4 Well hot food table with extended top and base with open base and apron. Mobile modular design, singled sided.   Stainless steel top and base. Controls for heat lamps and hot wells mounted on apron. Factory wired for single connection cord and plug.

Accessories:

- Continuous Integral solid top tray slide flat surface with mitered edges to match Item # 37 size and shape as shown on plan.

- Single service buffet shield for served food over hot wells only

- Heat lamp, infra red strip w/ lights and infinite control

- Manifold drain connection to gate valve and extend to floor sink

- Line up locks

- 5” swivel casters

- Provide with flexible water hose connection.

- Open base storage with adjustable intermediate shelf

- Provide punch out in top for type 6 deck mounted filler faucet provided by FSEC.  (FSEC to send to Colorpoint for installation)

- Adaptable to accept sheet pans

- 6’ cord and plug

- Stainless Steel over shelf above breath shield

- 30” high to top of tray slide

- Extended parts and labor warranty

ITEM NO 39    	COLD SERVING UNIT, MOBILE

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	K60-CFMA

Status:          	In Contract

Serving Counter, Cold Food, Cafeteria, mobile modular design, single sided open base with apron, stainless steel top, refrigerated cold pan, 4-pan size, stainless steel cabinet base. Factory wire lights and controls to single cord and plug.

- Chamfered continuous solid stainless top with integral tray slide with edges at 30” AFF to match Item # 38.

- unit to be 30" high to top of tray slide

- Line up locks

- 5” swivel caster

- breath shield, single service

- 6’ cord and plug

- Open base design at rear with adjustable intermediate shelf

- Fluorescent Lights

- Adapter bars for cold pan

- Locate drain on end closest to hot food table

- Vent compressor on kitchen side

- 5 year compressor warranty

- Extended parts and labor warranty

ITEM NO 40    	MILK CABINET, REFRIGERATED

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	KBFD-8

Status:          	In Contract

Milk Dispenser w/ 8 crate capacity

- 5" casters concealed within body

- Lid Locks

- 6’ cord and plug

- Padlock hasp

- Corner bumpers

- Fiberglas body panels. Color to be determined by architect or selected by operator

- 5 year compressor warranty

- Extended parts and labor warranty

ITEM NO 41    	UTILITY CART

Quantity Req'd.: 	2

Manufacturer: 	Metro Equip

Model No.:       	BC1627-24G

Status:          	In Contract

Utility cart, confirm color with owner prior to ordering.

- 4” swivel casters

ITEM NO 42    	KETTLE & POT FILLER

Quantity Req'd.: 	1

Manufacturer: 	T & S, Inc.

Model No.:       	B-0610

Status:          	In Contract

Faucet, Service Sink,. Mount at 56” AFF>

ITEM NO 43	 - SPARE NUMBER -

ITEM NO 44    	CONDIMENT CART, MOBILE

Quantity Req'd.: 	2 (two)

Manufacturer: 	Lakeside

Model No.:       	706

Status:          	In Contract

Serving Counter, Utility Unit, mobile.

- Base cabinet to have lockable left and right hinged doors w/ cylinder locks

- Casters included in standard accessories

- Engraved condiment label pumps

- Unit to be 31” high to top of tray slide

- Laminate finish (color to be selected by architect)

- 7 qt cryovac dispenser

- Sanitary 3 qt pump lock

- Stainless steel pumps

ITEM NO 45    	CASHIER COUNTER

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	74-ST-MOD

Status:          	In Contract

Cashier Module solid top with open base, single sided

- Unit to be 70-3/8” long x 42” wide and 30” high

- Solid top w/ integral tray slide and mitered right end.

- Open base storage with adjustable intermediate shelf

- Open at one end to accept chair as shown in plan

- 5” casters concealed in body

- Knock out in counter top w/ grommet to accept cords and data wires for POS system.

- Proivde with lockable cashier drawer

- Fiberglass panels over steel base (color to be determined by architect)

ITEM NO 46    	POS SYSTEM (NIC)

Quantity Req'd.: 	1

Manufacturer: 	By Owner

Model No.:       	POS-1

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

The item is shown on the drawing for informational purposes and generally represents the size/ capacity of unit to be provided by the vendor. Any utility connections indicated on drawings are representative and intended to assist the Engineer in planning base building utility systems. Utility requirements for existing equipment or equipment provided by a product supplier will be confirmed by the FSE Contractor and represented on the dimensioned rough-in plans for use by the construction trades.

ITEM NO 47    	OFFICE CHAIR (NIC)

Quantity Req'd.: 	3

Manufacturer: 	By Architect

Model No.:       	CHAIR

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

ITEM NO 48    	CASHIER COUNTER

Quantity Req'd.: 	1

Manufacturer: 	Low Temp Ind

Model No.:       	74-ST-MOD

Status:          	In Contract

Cashier Module solid top with open base, single sided

- Unit to be 70-3/8” long x 42” wide and 30” high

- Solid top w/ integral tray slide with mitered left end

- Open base storage with adjustable intermediate shelf

- Open at one end to accept chair as shown in plan

- 5” casters concealed in body

- Knock out in counter top w/ grommet to accept cords and data wires for POS system

- Fiberglass panels over steel base (color to be determined by architect)

- Provide with lockable cashier drawer.

ITEM NO 49    	POS SYSTEM (NIC)

Quantity Req'd.: 	1

Manufacturer: 	By Owner

Model No.:       	POS-1

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

The item is shown on the drawing for informational purposes and generally represents the size/ capacity of unit to be provided by the vendor. Any utility connections indicated on drawings are representative and intended to assist the Engineer in planning base building utility systems. Utility requirements for existing equipment or equipment provided by a product supplier will be confirmed by the FSE Contractor and represented on the dimensioned rough-in plans for use by the construction trades.

ITEM NO 50    	OFFICE COMPUTER (NIC)

Quantity Req'd.: 	1

Manufacturer: 	By Owner

Model No.:       	COMPUTER

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

ITEM NO 51	 - SPARE NUMBER -

ITEM NO 52    	WALK-IN FREEZER

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	Custom

Status:          	In Contract

Refrigerated Storage Unit, Walk-in, low-temperature (-10F) for installation in floor depression. of size and shape as shown on plan x 9’-2.25” overall height (nominal). 4” urethane wall and ceiling panels, U.L. Flame Spread 25 insulation. Panels without wooden structural members. Hinged entrance doors to be flush type, hinged as shown on plan. Thru ceiling door electrical assembly as shown on detail E-1-4

- Floorless with flat bottom wall panels. Slab urethane, vapor barrier and quarry tile w/ minimum 4” setting bed by GC.

- 2-2” Slab urethane insulation by G.C.

- Floor finish to match kitchen floor

- 1 Lot Closure panels per detail CSR-2-1 with finish to match exposed wall finish (F.S.E.C.) to verify finished ceiling height

- 1 Lot trim strip where required to close wall gaps with finish to match that of exposed wall panels to from floor to ceiling (F.S.E.C.) to verify finished ceiling height

- 36”x84” door with third hinge

- diamond plate wainscot on all exposed surfaces 36” high

- bumper rail at 36”

- 14”x14” viewport with heater wire

- Stucco aluminum interior and exposed exterior

- Unexposed exterior to be galvalume

- Kason Dead bolt lock

- Automatic door close, Kason K-194

- Approved Lithonia light fixtures and switches per detail E-1-4, installed and wired by electrical division. (See electrical plan for quantity and location of lights and switches)

- Modularm 75B, recessed with thru ceiling door electrical as shown on detail E-1-4

- Anti condensate heaters in full perimeter of door  and frame

- Stainless steel corner guards where applicable

- Diamond tread kick plate 36” on interior and exterior of door

ITEM NO 53	 - SPARE NUMBER -

ITEM NO 54    	DESK (NIC)

Quantity Req'd.: 	1

Manufacturer: 	By Architect

Model No.:       	DESK

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

ITEM NO 55    	EVAPORATOR COIL, LOW TEMPERATURE

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	EL-160

Status:          	In Contract

Unit to be adequately sized to operate Item 52, Freezer Compartment @ -10° F.  Electrical hook-up and interconnecting of system to be by the Electrical Contractor.

- Heat tape for low temp coil drain line furnished and installed by the FSE Contractor.  Final electrical connection to heat tape by Electrical Division.

ITEM NO 56    	CONDENSING UNIT, AIR COOLED

Quantity Req'd.: 	1

Manufacturer: 	Kolpak Ind Inc

Model No.:       	PR304L

Status:          	In Contract

F.S.E.C. to provide the necessary refrigeration lines required to operate and maintain the refrigeration system for Item 52, freezer compartment. Unit to be part of the remote refrigeration system for Item 55, Evaporator Coil.

F.S.E.C. to coordinate with the electrical/plumbing contractor to provide a complete and operable refrigeration system.

Provide start-up, five (5) year compressor warranty and one (1) year refrigeration service contract.

Division 16 to wire to safety disconnect switch.

- Unit to be located Janitor Closet unless otherwise specified by Architect.

- Assume a 30' refrigeration line run.

- Loose timeclock (freezer only) installed above walk-in freezer.

- Protective cover for "inside" application.

ITEM NO 57    	SECURITY SAFE (NIC)

Quantity Req'd.: 	1

Manufacturer: 	By Owner

Status:          	By Owner/Operator

This item is not in contract. It is provided by Owner. The specification is for reference only.

ITEM NO 58    	MOP HOLDER, 3-SPRING

Quantity Req'd.: 	1

Manufacturer: 	IMC/Teddy

Model No.:       	MH3

Status:          	In Contract

Mop Holder, 3-Spring.

- Furnish per manufacturer's standard specifications.

ITEM NO 59    	MOP SINK, HEAVY DUTY

Quantity Req'd.: 	1

Manufacturer: 	IMC/Teddy

Model No.:       	FS-H

Status:          	In Contract

Mop Sink, Heavy Duty.

- Service sink wall faucet (SSF).

- Hose, 36" long (HA).

ITEM NO 60    	AIR CURTAIN, UNHEATED

Quantity Req'd.: 	1

Manufacturer: 	Mars Air Doors

Model No.:       	72NCH-2

Status:          	In Contract

Note:  Motor control panels are required for all 3 Ph & any 1 Ph motors w/combined cap. greater than 1 HP.OR 20 AMPS; multiple units over single opening use 1 control panel per operating door

- Door Micro Switches are used for instant ON/OFF control; with door open air curtain is on, when door closed air curtain is off

Options:

- Micro Switch Combination (both plunger and roller all in one) (for all types of doors).

- Motor Control Panel for two motors, for any voltage and HP, supplied with NEMA 1 Cabinet with HOA selector switch on the cover and are remote mounted

- Housing Color To be selected by architect or operator.

Note: for N.S.F. air curtains specify NCH or NHV models, consult price book.

ITEM NO 61    	MOP BUCKET (NIC)

Quantity Req'd.: 	1

Manufacturer: 	Rubbermaid

Model No.:       	6186

Status:          	By Owner/Operator

This item is not in contract. The specification is for reference only. The item is shown on the drawing for informational purposes and generally represents the size/ capacity of unit to be provided by the Owner.