SECTION 100 - GENERAL PROVISIONS

TABLE OF CONTENTS								PAGE

101	GENERAL PROVISIONS							100-1

102	DEFINITIONS AND ABBREVIATIONS						100-1

102.1	Definitions							100-1

102.2	Abbreviations							100-4

102.3	Terms								100-5

102.4	Specifications by Reference					100-6

103	PURPOSE									100-6

103.1	Scope								100-6

103.2	Traffic Control						100-8

103.3	Street Cuts							100-9

103.4	Protection of Existing Facilities				100-9

103.5	Outages								100-10

103.6	Safety								100-10

104	SCOPE OF WORK								100-11

104.1	Work Conditions						100-11

104.2	Control of Work						100-11

104.3	Control of Materials						100-13

105	GENERAL CONDITIONS							100-13

105.1	Protection of Public and Utility Interests			100-13

105.2	Use of City Water						100-17

105.3	Pavement Cuts							100-17

106	PERMITS AND INSPECTIONS						100-17

106.1	Permits to Construct, Excavate or Obstruct a Public ROW	100-17

106.2	Fees								100-20

106.3	Inspection							100-21

106.4	Warranty							100-22

107	PLANS AND SPECIFICATIONS						100-23

107.1	Construction Plan Requirements				100-23

108	SPECIFICATIONS AND SUPPORT DOCUMENTATION				100-29

109	"AS-BUILT" DRAWINGS REQUIREMENTS					100-29

109.1	Certification Statement					100-29

109.2	"Record-Drawing" Information					100-29

109.3	Submittal of Certified "As-Built" Plans and Documents	100-30

CITY OF SCOTTSBLUFF - Standards and Specifications                                          June 1996

101	GENERAL PROVISIONS

These regulations shall be known as the City of Scottsbluff Standards and Specifications for the

Design and Construction of Public Improvements, 1996 Edition, and may be cited as such and shall

be referred to herein as the Standards and Specifications. They were adopted by the City of

Scottsbluff City Council on June 24, 1996.

102	DEFINITIONS AND ABBREVIATIONS

102.1  Definitions

Whenever the following terms are used in these Standards and Specifications they shall be

defined as follows:

Bonds - Performance, labor or material payment bonds, irrevocable letters of credit and

other instruments of security furnished to the City by the Responsible Party as surety in

accordance with the Developer's Agreement or other Agreements with the City.

City - The City of Scottsbluff, Nebraska, its City Council, the City Manager or the City

Manager's designee, or other official, body or agency designated by charter or ordinance

to act in its behalf.

City Engineer - The City of Scottsbluff Engineer who may be appointed by the City

Council, City Manager or its designee.

City Code - The latest, officially adopted City of Scottsbluff Municipal Code.

Common Facilities - Facilities serving, or held in common title, by the Responsible

Parties or occupants of two or more dwelling units or commercial or industrial

enterprises and covered by these Standards and Specifications.

Contractor - A person, partnership, corporation, or other legal entity who undertakes

to construct, install, alter, move, demolish, repair, excavate or add to any public

improvements or common facilities covered by these Standards and Specifications.

Includes subcontractors.

Controller - A complete electrical or solid state mechanism for controlling the operation

of a traffic signal, including the timer and all necessary auxiliary apparatus mounted in

a cabinet. (see also - Irrigation Controller).

Coordinated Control - operation of two or more traffic control signal installations with

definite interrelation.

Days - Calendar days, unless otherwise specified.

Developer - The person who is improving a parcel of land within the City and who may or

may not be the owner of said property.

Developer's Agreement - means an agreement by a developer with the City which clearly

establishes the developer's responsibility regarding project phasing, the provision of

public and private facilities and improvement and any other mutually agreed to terms and

requirements adopted by the City.

Director of Public Works - A person or firm appointed by the City Council, City Manager,

or his or her designee.

Equipment - All machinery and equipment, together with the necessary supplies for upkeep

and maintenance, and tools and apparatus, necessary for the proper construction and

acceptable completion of the work.

Final Acceptance - The date on which the City agrees to accept warranted work.

Fixed-Time Signal - A type of traffic control signal which directs traffic in accordance

with a predetermined time schedule.

gpcd - Gallons per capita per day.

gpm - Gallons per minute.

GRC - Galvanized Rigid Conduit.

Initial Acceptance - The date on which the City agrees to accept the work under contract;

this date usually follows the final walkthrough and completion of all "punch list" items,

and is also commonly referred to as the date of substantial completion. The warranty

period usually begins on the date of initial acceptance.

Inspector - The authorized representative of the City Engineer assigned to make detailed

inspection of construction work to assure compliance with these Standards and

Specifications and the plans as approved by the City.

Irrigation Controller - A fully automatic, electrically operated mechanism used to

regulate the timing of irrigation valve operations.

Lens - A part of the optical unit that redirects the light coming from the reflector.

It may be referred to as the redirecting cover glass or roundel.

MGD - Million gallons per day.

May - shall be interpreted as being permissive unless otherwise stated by the City

Council, Mayor or his or her designee.

Normal Work Hours - 7:30 a.m. - 4:00 p.m., Monday through Friday, except holidays.

Owner - Any individual, corporation, partnership, or other legal entity holding

controlling title on property which is the subject of improvements covered by these

Standards and Specifications or which are intended to come under the ownership or

control of the City.

Planning and Building Official - The Planning and Building Official of the City of

Scottsbluff or his or her designee.

Plans - Profiles, cross sections, drawings, and supplemental drawings, approved by

the City which show the locations, character, dimensions or details of the work.

psi - Pounds per square inch.

Public Improvements - Improvements under the ownership or control of the City including

but not limited to the components of the water system, sewer system, street system,

park system, and storm drainage system covered by these Standards and Specifications.

The term also includes similar improvements being built in connection with a

subdivision which are intended to be dedicated to the City.

PVC (Polyvinyl Chloride) - A strong, tough plastic based on resins made by the

polymerization of vinyl chloride or copolymerization of vinyl chloride with minor

amounts (not over 50%) of other unsaturated compounds, which are fashioned into

sheets, tubing, pipe, conduit, containers, insulation, etc.

Responsible Party - Any individual, corporation, partnership or other legal entity

involved in developing improvements covered by these Standards and Specifications.

Includes subcontractors, contractors, developers, and owners, as applicable in the

development process.

Right-of-way (ROW) - An area dedicated to public use for pedestrian, equestrian or

vehicular movement; railroads; public utilities; water and sanitary sewer

facilities and storm sewer facilities.

Service Area - shall mean that area, whether inside or outside city limits, that

receives water and/or sanitary sewer service from the City of Scottsbluff.

Shall - shall be interpreted as being mandatory.

Special Provisions - Special directions, provisions or requirements peculiar to the

project and not otherwise detailed or set forth in the specification.

Standards and Specifications - The body of directions, provisions, and requirements

contained herein, describing the method or manner of construction and the qualities

and  quantities of the materials and work to be furnished.

Street Superintendent - The Street Superintendent of the City of Scottsbluff or his or

her designee.

Supplier - An individual, firm or corporation having a direct contract with a

Responsible Party including any subcontractor for the manufacture or furnishing of

any part of the supplies and/or materials to be used at, or incorporated in, work at

the site.

Traffic Engineer - A person or firm appointed by the City Council, City Manager or his

or her designee.

Traffic Signal - A power-operated traffic control device, not a sign, by which traffic is

warned or is directed to take some specific action.

Warranty Period - shall be the time frame during which the Responsible Party is held

liable for all work performed and materials utilized prior to final acceptance by the

City of Scottsbluff. Typically one year after acceptance of any public improvements by

the City Council, City Manager or his or her designee.

Wastewater Superintendent - The Wastewater Superintendent of the City of Scottsbluff or

his or her designee.

Water Superintendent - The Water Superintendent of the City of Scottsbluff or his or her

designee.

102.2	Abbreviations

AAN - American Association of Nurserymen

AASHTO - American Association of State Highway and Transportation Officials

ACI - American Concrete Institute

AISC - American Institute of Steel Construction

ANSI - American National Standards Institute

APWA - American Public Works Association

ASA - American Standards Association

ASLA - American Society of Landscape Architects

ASTM - American Society for Testing and Materials

AWWA - American Water Works Association

CMP - Corrugated Metal Pipe

CMPA - Corrugated Metal Pipe Arch

DIP - Ductile Iron Pipe

FEMA - Federal Emergency Management Agency

FHWA - Federal Highway Administration

FIRM - Flood Insurance Rate Map

HERCP - Horizontal Elliptical Reinforced Concrete Pipe

IMSA - International Municipal Signal Association

ITE - Institute of Transportation Engineers

MUTCD - Manual on Uniform Traffic Control Devices

NDOR - Nebraska Department of Roads

NEC - National Electrical Code

NEMA - National Electrical Manufacturers Association

NOAA - National Oceanic and Atmosphere Administration

OSHA - Occupational Safety and Health Act

RCBC - Reinforced Concrete Box Culvert

RCP - Reinforced Concrete Pipe

SCS - Soil Conservation Service

SPP - Structural Plate Pipe

SPPA - Structural Plate Pipe Arch

UD&FCD - Urban Drainage and Flood Control District

UL - Underwriters Laboratories, Inc.

USDA - United States Department of Agriculture

USGS - United States Geological Survey

102.3	Terms

Whenever, in these Standards and Specifications the words "as ordered", "as directed",

"as required", "as permitted", "as allowed", or words or phrases of like meaning are

used, it shall be understood that the order, direction, requirement, permission, or

allowance of the City is intended.

Similarly, the words "approved", "reasonable", "suitable", "acceptable", "properly",

"satisfactory", or words of like meaning, unless otherwise specified herein, shall

mean approved, reasonable, suitable, acceptable, proper, or satisfactory in the

judgement of the City.

Whenever, in these Standards and Specifications, the words "City Engineer" or

"Traffic Engineer" are used, it shall be understood that the City employee named

therein shall be whoever is designated by the City Manager.

102.4	Specifications by Reference

All applicable specifications of agencies or organizations listed in subsection 102.2

are made a portion of these Standards and Specifications by reference and shall be the

latest edition or revision thereof.

103	PURPOSE

The purpose of these Standards and Specifications is to provide minimum standards to safeguard

life of limb, health, property and public welfare by regulating the design of, construction of,

choice of materials used for, location of, maintenance and use of all public improvements and

common facilities. These include, but are not limited to, sanitary sewer systems, water supply

systems, private utility service lines to water and sewer, public and private storm drainage

systems, streets, open space, parks and recreation facilities, traffic signals and devices,

public and private parking lots and appurtenances thereto. All equipment and material shall be

new unless approved by the City.

103.1	Scope

The provisions of these Standards and Specifications shall apply to the planning,

design, construction, enlargement, alteration, moving, removal, conversion, demolition,

repair, and excavation of any public improvements or common facilities specifically

regulated herein. These Standards and Specifications present the minimum standards

for construction of public improvements completed by Responsible Parties which are

intended for dedication to and ownership by the City. These Standards and Specifications

do not relate to the City's Capital Improvement Projects. With the exception of

maintenance practices, the City shall follow these Standards and Specifications where

practicable. These Standards and Specifications include the Utility Standards and

Specifications as adopted by the City.

In the case of those improvements that are required by the City, and are not

specifically covered in these Standards and Specifications, the City will require the

Responsible Party to follow applicable local, state and federal guidelines, or

standards promulgated by professional organizations. The City Engineer should be

consulted for guidance on proper references.

Alterations, additions, or repairs to existing improvements shall comply with all

requirements of these Standards and Specifications, unless specifically exempted

by the City Engineer.

(a)  Alternate Materials and Methods of Construction

The provisions of these Standards and Specifications are not intended to prevent

the use of any material or method of construction not specifically prescribed by

these procedures, provided any alternate is approved in writing by the City

Engineer and thus authorized by the City.

The City Engineer shall require that sufficient evidence or proof be submitted

to substantiate any request that may be made regarding the alternate method or

material. The details of any action granting approval of an alternate shall be

recorded and entered in the files of the City.

(b)	Variances

Whenever there are practical difficulties involved in carrying out the

provisions of these Standards and Specifications, the City Engineer may grant

variances for individual cases, provided that the City Engineer shall first

find that a special individual reason makes these procedures impractical and

that the variance is in conformance with the intent and purpose of these

Standards and Specifications, and providing that such variance does not lessen

any design requirement or any degree of integrity and shall result in a level of

safety, service and quality equal to or greater than that intended by the

application of the Standards and Specifications minimum requirements. The details

of any action granting modifications shall be recorded and entered in the files

of the City.

(c)	Tests

Whenever there is insufficient evidence of compliance with any provisions of

these Standards and Specifications or evidence that any material or construction

does not conform to the requirements herein, the City Engineer shall require that

the Responsible Party, at their expense, have tests performed which shall be used

as proof of compliance. These methods shall be as specified by these Standards

and Specifications or by other recognized test standards approved by the City

Engineer. If there are no recognized and accepted test methods for the proposed

alternate, the City Engineer shall determine test procedures. All tests shall be

made by an approved agency prior to testing by the City Engineer. Reports of such

tests shall be retained by the City.

(d)	Organization and Enforcement

The City Engineer is authorized and directed to enforce all provisions of these

Standards and Specifications. The City Engineer may appoint a civil engineer,

construction inspector, streets operations supervisor, police officer or other

related technical officer or inspector, or other employee to act as an

authorized representative.

Whenever any work is being done contrary to the provisions of these Standards

and Specifications, the City Engineer may order the work stopped by a written

notice which shall be served on any persons engaged in the doing or causing of

such work to be done, and any such persons shall forthwith stop such work until

authorized by the City Engineer to proceed.

(e)	Liability

The City Engineer, or an authorized representative, charged with the

enforcement of these Standards and Specifications, acting in good faith and

without malice in the discharge of these duties, shall not thereby be

rendered personally liable for any damage that may accrue to persons or

property as a result of any act or by reason of any act or omission in the

discharge of these duties.

(f)	Violations

It shall be unlawful for any person, firm, or corporation to construct,

enlarge, alter, repair, move, improve, remove, excavate, convert, or

demolish any public improvements or common facilities or permit the same to be

done in violation of these Standards and Specifications. Contractors who violate

these Standards and Specifications shall be subject to legal action which may be

initiated by the City of Scottsbluff.

(g)	No Waiver of Legal Rights

The City shall not be precluded or estopped by any measurement, estimate, or

certificate made either before or after the completion and acceptance of the work

from showing the true amount and character of the work performed and materials

furnished by the Responsible Party, or from showing that any such measurement,

estimate or certificate is untrue or incorrectly made, or that the work or

materials do not conform in fact to these Standards and Specifications.

103.2	Traffic Control

The flow of traffic on public streets and roadways shall be maintained at all times

during construction in accordance with the rules, regulations and conditions as issued by

the Traffic Engineer. All devices and procedures shall comply with the current edition of

the Manual on Uniform Traffic Control Devices.

The Responsible Party shall be responsible for the provision of a safe travelway on

all roadways on and adjacent to the job site. The Responsible Party shall erect or

cause erection of proper traffic control warning devices around all excavations,

embankments and obstructions and shall be responsible for the proper maintenance of

said erected devices, in accordance with the approved traffic control plan.

The Responsible Party shall cause suitable warning lights or flares to be provided and

kept lighted at night or other times when visibility is limited.

The Responsible Party shall provide flagmen and/or off-duty police protection as may be

determined by the Traffic Engineer for the protection of the public, as well as workers

on the job site.

The Responsible Party shall coordinate with the Traffic Engineer so that arrangements

may be made by the Responsible Party for detours, parking, access to property adjacent

to work, etc., 48 hours prior to their need.

The Responsible Party shall not close any street or work within any portion of a street

ROW without receiving approval from the Traffic Engineer 48 hours prior to such closure.

It is the Responsible Party's responsibility to notify the Police and Fire Departments

having jurisdiction in the area of construction 24 hours prior to closing any street,

alley, or fire lane which has been authorized for closure by the Traffic Engineer. The

Responsible Party shall also notify the Police and Fire Departments immediately after

opening of any street, alley, or fire lane.

The Traffic Engineer shall close down work which is not controlled in accordance with

approved City barricading procedures or on projects which require approval from the

Traffic Engineer, which has not been obtained by the Responsible Party.

No work shall be allowed at signalized intersections or on other arterial roadways

which impedes normal traffic flow from 6:00 a.m. to 8:30 a.m., and 3:30 p.m. to 6:00

p.m., except during emergencies or with prior approval of the Traffic Engineer.

103.3	Street Cuts

The removal of pavement, sidewalks, driveways or curb and gutter shall be performed

in a neat and workmanlike manner. Where utilities must cross these facilities, the

exact width of the cut shall exceed the width of the trench at the subgrade by at

least 12 inches on either side of the cut. Portland Cement concrete or asphaltic

concrete surfaces shall be cut with a pavement saw to a depth of four inches, or

more than one-half existing thickness as requested by the City Engineer, prior to

breaking. Cutting shall be limited to straight liens and acute angles shall be

avoided.

Within streets pavement, driveways or street curbing areas, at the discretion of the

Engineer, native material may be used to within two feet of asphalt grade. Should

the native material be deemed unsuitable by the City Engineer, then the entire

trench shall be backfilled with granular backfill approved by the Engineer, placed and

compacted in lifts of six inches or less. The replacement of Portland Cement concrete

sidewalks, driveways or curb and gutter shall be to the same horizontal dimensions as

that removed for the utility installation. Portland Cement concrete sidewalks shall

have a minimum thickness of four inches and a thickening to six inches at driveway

locations. Portland Cement concrete driveways shall have a minimum thickness of

six inches.

Prior to proceeding with any work within the public right-of-way, the Responsible

Party shall obtain and submit for review a street cut application permit from the

City. The City shall specify minimum pavement sections for replacement on the basis

of standards developed by the City and the classification of the street cut for

utility installation.

Portland Cement concrete design mix shall conform to any and all applicable City

standards regarding streets, curb and gutter and sidewalks.

103.4	Protection of Existing Facilities

The Responsible Party shall notify the electrical and gas utility, telephone company,

cable television, and all other interested parties prior to beginning work and shall

have their facilities staked and located in the field in order to ensure that there

shall not be interruptions of these services during progress of the work. Existing

power lines, telephone lines, trees, shrubbery, fences, water mains and services, gas

mains and services, sewer mains and services, cables, conduits, drainage and irrigation

ditches and pipes, embankments and other structures in the vicinity of the work not

authorized to be removed, shall be supported and protected from damage by the

Responsible Party during the construction and until completion of work.

The Responsible Party shall preserve intact any underground pipes or other utilities

encountered during construction. The Responsible Party shall be liable for all damages

done to such existing facilities and structures and shall save the City harmless from

any liability or expense for injuries, damages or repairs to such facilities. The type,

size, approximate location and number of all known underground utilities may be shown

on all drawings. It shall be the responsibility of the Responsible Party to verify the

existence and location of all underground utilities along the route of the work.

In the event that it is determined during construction, through potholing or other

appropriate method, that any underground utility conduit, including sewers, water mains,

gas mains and drainage structures or any above ground utility facilities are required to

be relocated, the Responsible Party shall notify the utility owner well in advance of

approaching such utility so that arrangements with the City and/or owners of the affected

utility can be made without delay to the work. All relocations shall be done at the

designated party's expense and upon approval by the City Engineer.

103.5	Outages

In the event loss of service is necessary, the Responsible Party shall notify the City at

least 48 hours in advance. Such services shall in no case be interrupted for more than

four hours. Outages for school, medical clinics and various commercial businesses must

be conducted at approved times as specified by the owner or chief administrator of such

establishments and upon approval by the City Engineer. If outages for more than four

hours are necessary, they must be conducted at times to cause the least inconvenience to

the customers and upon the approval of the City Engineer. Under all circumstances, work

must be continuous until all customers are back in service. If, in the process of

installing a connection, there exists an industry or building that cannot be out of

water, as designated by the City Engineer, such as a hospital, appropriate temporary

means shall be taken to provide and convey water. The water and means of conveyance

shall be approved by the City Engineer and be at the Responsible Party's expense.

103.6	Safety

Machinery, equipment, materials and all hazards shall be guarded or eliminated in

accordance with the "Manual of Accident Prevention in Construction" of the Associated

General Contractors of America and all applicable Federal regulations, including OSHA,

state, county and municipal laws. No blasting shall be done without the approval of

the City. Safety equipment, devices and clothing shall be utilized by personnel where

required by federal, state and local laws.

104	SCOPE OF WORK

104.1	Work Conditions

(a)	Emergency Work

When, in the opinion of the City Engineer, the Responsible Party has not taken

sufficient precautions for the safety of the public or the protection of the work

to be constructed, or of adjacent structures or property which may be damaged by

processes of construction on account of such neglect, and an emergency may

arise and immediate action is considered necessary in order to protect public or

private interests, the City Engineer, with or without notice to the Responsible

Party, may provide suitable protection by causing such work to be done and

material to be furnished and placed as the City Engineer may consider necessary

and adequate. The cost and expense of such work and material so furnished shall

be borne by the Responsible Party and shall be paid within 30 calendar days upon

presentation of the invoice by the City.

The performance of such emergency work under the direction of the City Engineer

shall in no way relieve the Responsible Party of responsibility for damages which

may occur during or after such precaution has been taken.

In an emergency threatening loss of life or extensive damage to the work or to

adjoining property, and where the Responsible Party is unable to obtain special

instructions or authorization from the City Engineer after diligent attempts to

obtain such special instruction or authorization in sufficient time to take the

necessary action, the Responsible Party is hereby permitted to act to prevent

such threatening loss or damage.

(b)	Final Cleanup

The Responsible Party shall be responsible for daily clean-up on the project area

and shall remove and properly dispose of all surplus and discarded materials,

rubbish, and temporary structures from the project area and adjacent areas, and

where appropriate leave the project area swept and in a neat and presentable

condition. The Responsible Party shall restore all work areas which have been

damaged by the operations, to general conformity with the specifications for the

item or items involved, and to the original condition.

Responsible Party shall be responsible for keeping streets free of dirt, mud, and

any debris during construction, as required by current City codes/regulations,

and State regulations.

The Responsible Party shall inspect and clean the interior of all manholes and

catchbasins within the construction limits or impacted by the construction therein

by the activities of the Responsible Party.

104.2	Control of Work

(a)	Authority of City Engineer

The City Engineer shall have the authority to stop the work whenever such stoppage

may be deemed necessary. The City Engineer shall resolve all questions which arise

as to the quality and acceptability of materials furnished, work performed,

interpretation of the plans and specifications, and acceptable fulfillment of the

requirements of these Standards and Specifications.

The City Engineer shall resolve all questions which may arise relative to the

performance of the work with respect to these Standards and Specifications.

(b)	Authority and Duties of Inspector

Inspectors are authorized to inspect all work completed and all material furnished.

Inspections may extend to all or any part of the work and to the preparation,

fabrication, or manufacture of the materials to be used. The inspector is not

authorized to revoke, alter, or waive any requirements of these Standards and

Specifications. The inspector is authorized to call the attention of the

Responsible Party to any failure of the work or materials to conform to these

Standards and Specifications. The inspector shall have the authority to reject

materials until any questions at issue can be resolved by the City Engineer.

The Inspector shall, in no case, act as foreman or perform other duties for the

Responsible Party, or interfere with the management of the work done by the

Responsible Party. Any "advice" which the Inspector may give the Responsible

party shall not be construed as binding upon the City Engineer or the City in

any way, or release the Responsible Party from fulfilling all of the terms of

these Standards and Specifications.

The presence or absence of the Inspector shall not relieve, in any degree, the

responsibility or the obligation of the Responsible Party.

The City Engineer, or an authorized representative, shall, at all times, be provided

reasonable and safe access to inspect the work whenever it is in preparation or

progress.

(c)	Responsible Party's Responsibility for Work

In case of suspension of work for any cause whatever, the Responsible Party, before

leaving the job site, shall take such precautions as may be necessary to prevent

damage to the project, provide for proper drainage and erect any necessary

barricades, signs, or other facilities, at the Responsible Party's expense, as

directed by the City Engineer.

(d)	Removal of Unauthorized and Unacceptable Work

Work which does not conform to the plans and specifications, and which results in

an inferior or unsatisfactory product, shall be considered unacceptable work.

Unacceptable work, whether the result of poor workmanship, use of defective

materials, damage through carelessness or any other cause, found to exist prior to

the final acceptance of the work, shall be immediately removed and replaced or

corrected by, and at the expense of, the Responsible Party. This expense includes

total and complete restoration of any disturbed surface to original or better than

the original condition which existed before the repairs or replacement, regardless

of improvements on lands where the repairs or replacement are required.

104.3	Control of Materials

(a)	Samples and Tests

To ascertain that materials comply with contract requirements, samples shall be

taken at the source or at the job destination, as often as the City Engineer deems

it necessary. Taking of samples shall be in accordance with standard practices

except where methods and procedures for sampling materials are otherwise set

forth in these Standards and Specifications.

The Responsible Party shall furnish, without charge, all samples required by the

City Engineer and shall afford such facilities and means as may be necessary for

collecting and forwarding them. The Responsible Party may be required to furnish,

when requested by the City Engineer, a written statement giving the origin,

composition and process of manufacture of a material.

Any samples taken, or tests conducted upon the samples, shall be at the

expense of the Responsible Party.

(b)	Storage of Materials

Materials shall be stored so as to insure the preservation of their quality and

suitability for the work. Stored materials, even though inspected prior to storage,

shall be subject to inspection prior to their use in the work and shall meet all

requirements of these Standards and Specifications at the time they are used.

Stored materials shall be located so as to facilitate inspection. With the City

Engineer's approval, portions of the right-of-way not required for public travel

may be used for storage purposes and for the placing of the Responsible Party's

materials and equipment. Any additional space required shall be secured by, and at

the expense of, the Responsible Party.

(c)	Defective Materials

Materials not in conformance with the requirements of these Standards and

Specifications shall be considered defective and shall be rejected. Rejected

materials shall be removed from the work site.

105	GENERAL CONDITIONS

105.1	Protection of Public and Utility Interests

(a)	Public Convenience and Safety

Fire hydrants shall be visible and accessible to the Fire Department from the street

at all times. No permanent or temporary obstructions (including, but not limited to,

fencing, street lighting, landscaping, and mailboxes) shall be placed within three

feet of a fire hydrant.

Unless otherwise specified, the Responsible Party shall give notice, in writing, to

the proper authorities in charge of streets, gas and water pipes, sanitary and storm

sewer facilities, electric service, cable television and other conduits, railroads,

poles, manholes, catchbasins and all other property that may be affected by the

Responsible Party's operations, at least 48 hours before breaking ground. The

Responsible Party shall not hinder or interfere with any person in the protection

of such property, or with the operation of utilities at any time. The Responsible

Party must obtain all necessary information in regard to existing utilities,

protect such utilities from injury, and avoid unnecessary exposure so that they

shall not cause injury to the public.

The Responsible Party shall obtain all necessary information in regard to the

planned installation of new utilities and cables, conduits and transformers,

make proper provision and give proper notification so that new utilities and

electrical equipment can be installed at the proper time without delay to the

Responsible Party or unnecessary inconvenience to the Responsible Party. All

underground utilities and electrical equipment shall be installed prior to the

placement of the final lift of pavement.

When the work involves excavation adjacent to any properties or structures along

the work site, the Responsible Party shall give property owners due and sufficient

written notice thereof, and shall furnish a copy to the City.

(b)	Protection and Restoration of Property and Monuments

The Responsible Party shall use every precaution to prevent the damage or

destruction of public or private property adjacent to or interfering with the

work, such as poles, trees, shrubbery, crops, fences, and monuments; and all

overhead structures such as wires and cables, within or outside of the right-

of-way.

The Responsible Party shall protect and support all water, gas, sanitary sewer,

storm sewer, electrical pipes and conduits, railroad tracks, buildings, walls,

fences, landscaping, significant wetlands, or other properties which are liable

to be damaged during the execution of his work. All reasonable and proper

precautions to protect property, persons, animals, and vehicles from injury

shall be taken. Wherever necessary, fencing or railing shall be placed around any

excavation and a sufficient number of amber lights shall be kept burning from

twilight until sunrise. One or more guards shall be employed as additional security

wherever they are needed or required by the City Engineer.

The Responsible Party shall not prevent the flow of water in the gutters of the

street and shall use proper means to permit the flow of surface water along the

gutters while the work is progressing.

The Responsible Party shall protect and carefully preserve all land boundary and all

survey control monuments until the Responsible Party or an authorized surveyor has

referenced their location for relocation. All monuments disturbed or removed by the

Responsible Party or subcontractors, through negligence or carelessness, shall be

replaced by a licensed surveyor and approved by the City Engineer, at the

Responsible Party's expense.

No person shall remove or disturb any grade or line stakes or marks set by the City

Engineer or an authorized representative without approval.

The Responsible Party shall be responsible for the damage or destruction of property

resulting from neglect, misconduct, or omission in the manner or method of execution

or non-execution of the work, or caused by defective work or the use of

unsatisfactory materials. They shall restore such property to a condition similar to

or better than that existing before such damage or injury was done, by repairing,

rebuilding, or replacing it as may be directed, or they shall otherwise make good

such damage or destruction in an acceptable manner.

Responsible Party shall bear the cost of repairing underground pipes, wires, or

conduits damaged by the work. The repair shall be performed by the City and other

appropriate utility companies, in coordination with the City.

Responsible Party shall be liable for all project damage caused by storms and fire,

and shall under no circumstances start fires.

Responsible Party shall ensure the continued availability of public services,

including but not limited to postal, solid waste collection, emergency services,

and public utilities.

(c)	Survey Monuments

Permanent survey monuments shall be set at locations approved by the City Engineer,

on all new subdivision plats in accordance with the City of Scottsbluff Subdivision

Ordinance, as amended, and as required and approved by the City.

(d)	Use of Explosives

When blasting is permitted and approved in writing by the Chief of Police, Chief of

the Fire Department, and the City Engineer, the Responsible Party shall use the

utmost care to protect life and property. Signals warning persons of danger shall

be given before any blast, in accordance with all local, state and federal

regulations.

Excessive blasting or overshooting shall not be permitted. The City Engineer shall

have authority to order discontinuing any method of blasting which leads to

overshooting, is dangerous to the public, or destructive to property or to natural

features.

Before any blasting shall be done by the Responsible Party, a certificate of

insurance indicating special blasting coverage in the following minimum amounts

shall be filed with the City:

Property Damage, each accident     $1,000,000.00

Single limit or equivalent,        $1,000,000.00

each accident

(e)	Protection of Streams, Lakes and Reservoirs

The Responsible Party shall take all necessary precautions to prevent pollution of

streams, lakes, reservoirs and irrigation ditches with fuels, oils, bitumens, sodium

chloride, calcium chloride, or other harmful materials. The operations shall be

conducted and scheduled to avoid or minimize siltation of streams, lakes and

reservoirs. A plan for erosion protection including copies of Storm Water Permit

when required by NDEQ shall be submitted to the City Engineer for approval before

starting work and must conform to all local, state and federal regulations.

(f)	Dustproofing

The Responsible Party shall take all necessary steps to control dust arising from

operations connected with the work. When ordered by the City Engineer, the

Responsible Party shall dustproof the construction area by sprinkling, as directed

by the Engineer, at the Responsible Party's expense.

(g)	Barricades, Warning Signs and Flagman

All work shall be barricaded as necessary at all times. Between the hours of sunset

and sunrise barricades shall be properly lighted to warn all persons. All signs,

barricades, lights, and warning devices shall be constructed and used in accordance

with the Manual on Uniform Traffic Control Devices, at the Responsible Party's

expense.

Responsible Party shall be responsible for providing a traffic control plan to the

City Engineer before beginning work.

The Responsible Party shall be responsible for all damages to the work due to

failure of barricades, signs, lights, and flaggers and other workers to protect

it, and whenever evidence of such damage is found prior to acceptance, the City

Engineer may order the damaged portion immediately removed and replaced by the

Responsible Party.

The Responsible Party shall be responsible for furnishing, erecting and

maintaining those traffic control devices and facilities, as required above,

throughout the life of the contract, including periods of suspension and, if

necessary, during the warranty period.

105.2	Use of City Water

If the Responsible Party requires City water for any part of the project, these steps

must be taken:

1.	Obtain permission from the City Water Department Superintendent.

2.	Pay a refundable deposit, all monthly rental and water usage charges, and pay for

all damages other than normal wear and tear to the hydrant, meter, street or other

public improvements that may result from the hydrant use.

3.	Return the hydrant meter immediately when no longer required.

4.	The hydrant meter may only be used at the approved fire hydrant location approved

by the Water Superintendent. Use of a hydrant at another location must receive

prior approval from the Water Superintendent as well.

105.3	Pavement Cuts

If a pavement cut is required, the Responsible Party shall install a permanent, similar

to existing surfacing patch within 24 hours following completion of the work. The

Responsible Party shall place a temporary, cold mix, asphalt patch in all street cuts as

deemed necessary and directed by the City Engineer, or an authorized representative,

immediately after completing backfill, if a permanent patch cannot be installed within 24

hours. The Responsible Party shall submit a schedule for the surfacing patch installation

to the City Engineer. The Engineer may require the Responsible Party to install flowcrete

(lean concrete) into the trench and backfill area. City Engineer shall determine those

areas prior to the initial pavement cut being permitted.

106	PERMITS AND INSPECTIONS

106.1	Permits to Construct, Excavate, or Obstruct a Public Right-Of-Way

It shall be unlawful for any person, firm or corporation to construct, enlarge, alter,

repair, move, improve, remove, excavate, convert or demolish any public improvements or

common facilities regulated by these Standards and Specifications without first

obtaining a contract or permit from the City of Scottsbluff. A building permit shall also

be obtained prior to the issuance of the right-of-way work permit for other than City

contract work. . A permit or City contract shall be required for all work in any

easement, right-of-way or property owned by the City.

(a)	Application for Permit

Applicants for right-of-way permits shall complete an application in writing on a

form furnished by the City for that purpose from the Scottsbluff Planning, Building

and Development Department. Each application shall be completed by the Responsible

Party.

Street Obstruction Permit Here

(b)	Right-Of-Way Work Permit Issuance

The application, plans, specifications, and other data filed by an applicant for a

permit shall be reviewed by the Planning and Building Official or his or her

designee. The plans may be reviewed by other departments of the City to verify

compliance with any applicable laws. If the Planning and Building Official finds

that the work described in an application for a right-of-way work permit and the

plans and other data filed therewith conform to the requirements of these Standards

and Specifications and other pertinent laws and ordinances and that all required

fees have been paid, a right-of-way permit shall be issued to the applicant.

When issuing a right-of-way work permit for which plans are required, the Planning

and Building Official shall endorse the plans in writing or by stamping the plans

and specifications. The approved plans and specifications shall not be changed,

modified, or altered without written authorization from the Planning and Building

Official, and all work shall be done in conformance with the approved plans and

specifications. One set of approved plans shall be maintained at the work site at

all times during the progress of the work.

The issuing and granting of a right-of-way work permit shall not be construed to be

a permit for, or an approval of, any violation of any of the provisions of these

Standards and Specifications or of any regulations of the City. No permit presuming

to give authority to violate or cancel the provisions of these Standards and

Specifications shall be valid.

The issuing of a right-of-way permit based on plans, specifications or other data

shall not prevent the Planning and Building Official or City Engineer from requiring

the correction of errors in said plans, specifications and other data, or from

stopping construction operations which are in violation of these Standards and

Specifications or any other regulations of this jurisdiction.

Right-of-way work permit fees shall be paid in full at the time of permit issuance.

The fees shall be as determined by the City Code of the City of Scottsbluff.

(c)	Permit Expiration

Every right-of-way work permit issued by the Planning and Building Official under

the provisions of this section shall expire if the work authorized by such a permit

is not substantially begun within six months from the date of the permit or if the

construction of work authorized by the permit is suspended or abandoned for a period

of six months at any time after the work is begun. Before such work can be resumed,

a new right-of-way work permit shall be first obtained and the fee required shall be

one-fourth of the amount required for a new permit to do such work, provided no

changes have been made or required by the Planning and Building Official in the

original approved plans and specifications.

Any permittee holding an unexpired right-of-way work permit may apply for an

extension of the time within which work may begin under that permit if the permittee

is unable to begin work within the time required by this section for good cause, and

that the cause is acceptable to the Planning and Building Official. The Planning and

Building Official may extend the time for action by the permittee for a period not

exceeding six months upon written request by the permittee, showing that

circumstances beyond the control of the permittee have prevented action from being

taken. No permit shall be extended more than one time. In order to renew action on

an expired right-of-way work permit the permittee shall pay a new, full permit fee.

(d)	Right-of-Way Work Permit Suspension or Revocation

The Planning and Building Official may suspend or revoke any permit, in writing,

issued under the provisions of these Standards and Specifications whenever the

permit is issued in error or on the basis of incorrect information supplied by the

applicant or whenever such permit may have been issued in violation of any ordinance

or regulation of any of the provisions of these Standards and Specifications. In the

event a permit is suspended or revoked, no refund of permit fees shall be made.

106.2	Fees

(a)	Plan Review Fees

Plan review fees shall be paid in full at the time plans and specifications for

approval by the Planning and Building Official. The plan review fees shall be as

determined by the City. Applications for which no permit is issued within six

months following the date of the application shall expire; and plans and other

data submitted for review may be returned to the applicant or destroyed by the

Planning and Building Official. The Planning and Building Official may extend

the time for action by the applicant for a period not exceeding six months upon

request by the applicant showing that circumstances beyond the control of the

applicant have prevented action from being taken. No application shall be

extended more than once. In order to renew action on an application after

expiration, the applicant shall resubmit plans and a new plan review fee for

reapproval by the Planning and Building Official.

(b)	Right-of-Way Work Permit Fees

The fee for right-of-way work permits shall be as determined by the City. Right-

of-way work permit fees shall be paid in full at the time the plans and

specifications have been approved by the Planning and Building Official and the

right-of-way permit is issued.

(c)	Investigation Fees (Working without a Permit)

Whenever any work for which a permit is required by these Standards and

Specifications has begun without the required permit having been obtained, a

special investigation shall be made before a permit may be issued for such work.

All work shall cease immediately upon written notice by the Planning and Building

Official.

An investigation fee shall be collected whether or not a permit is then or

subsequently issued. the investigation fee shall be as determined by the City. The

payment of such investigation fees shall not exempt any person from compliance with

all other provisions of these Standards and Specifications nor from any penalty

prescribed by law.

(d)	Fee Refunds

The Planning and Building Official may authorize the refunding of any fee which was

erroneously paid or collected. Upon written request from the Responsible Party, the

Planning and Building Official may authorize the refunding of not more than 80

percent of the inspection part of the permit fee when no work has been done under a

public improvement permit issued with these procedures.

The City Engineer shall not refund any fee except upon written application filed by

the original permittee. The written application must be filed not later than one

year after the date of the fee payment.

106.3	Inspection

All construction work for which a right-of-way work permit is required shall be subject

to inspection by the City Engineer and certain types of construction shall have

continuous inspection.

It shall be the responsibility of the person performing the work authorized by a permit

to notify the City Engineer that such work is ready for inspection. The City Engineer

shall require that every request for inspection be filed at least 48 hours before such

inspection is desired. Such request may be in writing or by telephone, at the option

of the City Engineer.

It shall be the responsibility of the person requesting inspections required by these

Standards and Specifications to provide access to and means for proper inspection of

all work.

(a)	Additional Inspections and Reinspections

The City Engineer may make or require additional inspections of any work as deemed

necessary to ascertain compliance with the provisions of these Standards and

Specifications and other provisions of the City Code.

A reinspection fee may be assessed for each inspection or reinspection when such

portion of work for which inspection is called is not complete or when corrections

called for have not been made.

This subsection is not to be interpreted as requiring reinspection fees the first

time a job is rejected for failure to comply with the requirements of these

Standards and Specifications, but rather as controlling the practice of calling for

inspections before a job is ready for such inspection or reinspection. Reinspection

fees may be assessed when the permit is not in the possession of the permit holder,

or an authorized agent, at the work site, when the approved plans are not readily

available to the inspector, for failure to provide access on the date for which

inspection is requested, or for deviating from plans approved by the City Engineer.

To obtain a reinspection, the applicant must submit a letter requesting reinspection

at least 48 hours in advance, and pay a fee as determined by the City. In instances

where reinspection fees have been assessed, no additional inspection of the work

shall be performed until the required fees have been paid.

106.4	Warranty

(a)	The Responsible Party is required to warranty all improvements for the previously

defined warranty period or as described in a Developer's Agreement. The initial and

final acceptance processes are also described in the Developer's Agreement.

(b)	Certain landscape improvements have special requirements for the warranty period

and final acceptance. These are described below:

1. 	For privately developed landscape seeding projects which are to be accepted by

the City, the Responsible Party shall maintain all seeded or sodded areas

through the end of the defined warranty period. The Responsible Party shall

maintain all seeded and sodded areas until initial acceptance; the City shall

maintain seeded areas following initial acceptance. Maintenance shall consist

of repair of eroded areas, watering, mowing, weeding, fertilizing, and

reseeding as necessary. For mowing operations, sound horticultural practices

shall be followed so that no more than one-third of the leaf surface is

removed during mowing and that the height of the grass is at least three

inches after the final cut. For initial acceptance of irrigated areas, no more

than 10 percent of the seeded areas shall have bare patches greater than one

foot. For initial acceptance of non-irrigated areas all seed shall be

germinated to the satisfaction of the City Inspector. Any areas deemed by the

City to be unacceptable shall be reseeded according to these Standards and

Specifications and shall be well-established prior to final acceptance, which

shall occur at the time of final acceptance for the entire project. Damage

to seeded or sodded areas during the warranty period which is caused by

overuse shall be exempt from this warranty coverage.

The City shall pay for all water use following initial acceptance; however,

any excessive water consumption, as determined by the City Engineer, shall be

paid for by the Responsible Party, at current market rates.

The Responsible Party shall erect suitable signs at important points notifying

the public to keep off of the seeded areas until seed is well established. Any

traffic damage that may occur prior to final acceptance of the work shall be

repaired and reseeded or resodded at the Responsible Party's expense.

2.	For privately developed landscape planting projects which are to be accepted

by the City, the Responsible Party shall be responsible for all maintenance

following installation of each plant and shall continue maintenance procedures

through the end of the one year warranty period. For publicly developed

projects, the Responsible Party shall maintain all planted areas until initial

acceptance; the City shall maintain such areas following initial acceptance.

This maintenance shall include watering, weeding, trimming, mulching, wrapping,

spraying, tightening or repairing of guy wires, removal of dead materials, and

resetting of plants to proper grades and upright positions as required. The

City shall pay for all water use following initial acceptance; however, any

excessive water consumption as determined by the City Engineer, shall be paid

for by the Responsible Party, at current market rates.

During the warranty period, the Responsible Party shall supply all supplemental

winter watering.

All trees, shrubs, groundcovers, and perennials shall be warranted for the

warranty period from the date of initial acceptance of the landscape

improvements. All annuals shall be warranted during their normal period of

growth. Any materials which must be replaced, as determined by the City, shall

be replaced within 30 days upon notification from the City.

3.	The entire irrigation system (including materials and workmanship) shall be

warranted for the warranty period from date of initial acceptance for the

system.

During the warranty period, the Responsible Party shall make all adjustments

to the system and perform all work required to maintain the designed function

of the system and to maintain the desired appearance of the landscape.

The Responsible Party shall properly winterize the system in the fall and

start up the system in the spring during the warranty period, in response to

local weather conditions or as directed by the City Engineer.

107	PLANS AND SPECIFICATIONS

Plans, engineering calculations, diagrams, traffic report, drainage report, pavement design

report and other data as required, including the City Development Permit, shall be submitted,

as required by the City Engineer, with each application for a permit. The City shall require

that plans, computations and specifications be prepared and designed by a professional engineer

or professional architect, licensed in the State of Nebraska; with the exception of landscape

and irrigation plans, which shall be prepared by a professional landscape architect.

An exception to this is that the City Engineer may waive the submission of plans, calculations,

or other analysis, if in the City Engineer's judgement, the nature of the work applied for is

such that reviewing of plans is not necessary to obtain compliance with these Standards and

Specifications.

107.1	Construction Plan Requirements

All construction plans shall be checked for conformance with City minimum design

standards prior to approval by the City. This approval shall be for conformance to City

design standards and other requirements; engineering design or needs shall remain the

responsibility of the professional design engineer. Two copies of the construction plan

shall be submitted to the City Engineer for approval. Once all review comments have been

addressed and the plans are final, the original shall be submitted for the City stamp of

approval. The stamped original and affixed stamped copy shall be returned to the

applicant. All construction plans shall be 18" x 24" or 24" x 36" in size, and shall be

on mylar or vellum.

Should circumstances warrant changes to the approved plans or specifications, a written

approval must be obtained from the City Engineer. Copies shall be given to the

Responsible Party, and the project's engineer. It shall be the duty of the engineer,

land surveyor, or preparer of the as-builts to record any and all changes on "as-

built" drawings at the completion of the project. Two (2) sets of "as-built', permanent

drawings shall be furnished to the City at the time of application for acceptance. "As-

Built" certification requirements are outlined in subsection 109.

(a)	General Requirements

Plan and specifications shall be drawn to scale and shall have sufficient clarity

to indicate the location, nature and extent of the work proposed and show in detail

that it shall conform to the provisions of these Standards and Specifications and

all relevant laws, ordinance, rules and regulations.

The following items shall be shown on all plans:

1.	Title Block (lower right-hand corner preferred).

2.	Scale (1"=100' horizontal and 1"=10' vertical for plans and profiles are a

minimum).

3.	Revision number and date.

4.	Name of professional engineer and firm.

5.	Professional Engineer's PE No.

6.	Drawing number(s).

7.	Statement:  "All work shall be constructed to City of Scottsbluff Standards

and Specifications. This approval is for conformance to these

Standards and Specifications and other City requirements. The

engineering design and concept remains the responsibility of the

professional engineer."

Approved:

City Engineer                       Date              Job No.

If irrigation ditches are involved, an approval block for the ditch company

shall be provided.

(b)	Plan Details

1.	North arrow, to the top of the page, on the right side.

2.	Property lines; indicate lots with lot number and block number to be served by

solid lines; other property lines dotted, survey monuments.

3.	Ownership or subdivision information.

4.	Street names, right-of-way, and easements with width dimensions.

5.	Existing utility lines (buried) location and depth water, gas, telephone, storm

drain, irrigation ditches, sanitary sewers, and other pertinent details, such

as houses, curbs, water courses, etc.

6.	Vicinity map.

7.	Overall water, sanitary sewer, storm water plan.

8.	All bench marks.

(c)	Profile Details

1.	Vertical and horizontal grids with scales.

2.	Ground surface existing (dashed) and proposed (solid).

3.	Existing utility lines.

4.	Bench marks (USGS Datum or City of Scottsbluff Datum) and project bench mark

denoted.

5.	Existing manhole invert and rim elevations.

(d)	Water Supply Construction Details

In addition to the above general plan and profile details, all water supply

construction plans shall include the following items:

1.	Proposed water mains:

Size

Length

Materials, types of joints, and proposed depth of main line

Location dimensions. Other items including elevation top of valve nut, rim

elevation of valve box or manhole, meter box, etc. may be required by City

Engineer.

2.	Fittings, for example;

Tees

Crosses

Reducers

Bends

Plugs

Blow-offs

3.	Valves.

4.	Fire Hydrants.

5.	Plan, profile and complete details for off-site transmission mains, pump

stations, special valves, and vaults, tanks, etc.

(e)	Sanitary Sewer Construction Details

In addition to the general plan and profile details, all sanitary sewer construction

plans shall include the following:

1.	Proposed sanitary sewer mains:

Diameters

Materials and types of joints

Gradients

Length between manholes

2.	Proposed manholes and cleanouts:

Stationing and other number designation

Elevation of inverts in and out of manhole

Elevation of manhole rim

Amount of fill through manhole

3.	Location control dimension.

4.	Manhole stub-outs.

5.	Proposed future extensions.

6.	Proposed wye and riser connection for services.

7.	Proposed service connections or stub-ins.

8.	Proposed underdrain.

9.	Proposed concrete encasement.

10.	Proposed cut-off walls.

(f)	Storm Drainage Construction Details

In addition to the above general plan and profile details, all storm drainage

construction plans shall include the following:

1.	Drainage area plan; an overall plan of the area under study showing:

a.  North arrow.

b.  Contours (maximum two foot intervals) on site and off site as required by

City Engineer.

c.  Location and elevation of City or USGS bench marks.

d.  USGS Datum or City of Scottsbluff Datum.

e.  Property lines.

f.  Boundary lines (counties, districts, tributary area, etc.).

g.  Streets and street names and approximate grades.

h.  Subdivision (name and location by section).

i.  Existing irrigation ditches.

j.  Existing drainage ways including gutter flow directions.

k.  Drainage sub-area boundaries.

l.  Easements required.

m.  Proposed curbs and gutters and gutter flow directions.

n.  Proposed cross pans and flow directions.

o.  Proposed piping and open drainage ways.

p.  Flow calculations for five and 100 year storm runoff.

q.  Path and plain of 100 year storm runoff flows delineated.

r.  Critical minimum finished floor elevations for protection from 100 year

runoff.

s.  Proposed inlet locations and inlet sizes.

t.  Floodplain information, indicating land in floodplain, and land not in

floodplain.

u.  Area grading plans for final stage.

2.	Proposed pipes

a.  Plan showing stationing.

b.  Profile.

c.  Size, lengths between manholes and type, material.

d.  Grades, capacity.

e.  Inlet and outlet details.

f.  Manhole details (station number and invert elevations).

3.	Proposed open channels and detention facilities

a.  Plan showing stationing.

b.  Profile.

c.  Grades, and capacities.

d.  Typical cross sections for both channels and ponds.

e.  Lining details.

4.	Proposed special structures (manholes, headwalls, trash gates, etc.)

a.  Plan.

b.  Elevation.

c.  Details of design and appurtenances.

5.	Complete material lists (submitted separately)

(g)	Street Construction Details

In addition to the above general plan and profile details, all street construction

plans shall include the following:

1.	Existing irrigation ditches to be removed or piped.

2.	Proposed curb, gutter and sidewalk.

3.	Proposed crosspans including flow direction.

4.	Storm drainage facilities.

5.	Location and elevation of USGS and City bench marks.

6.	Horizontal curve data, with radii, tangents, points of curvature, (P.C.),

intersection (P.I.) and tangency (P.T.).

7.	Typical section of street construction showing structure and dimensions.

8.	Stations and elevations of radius points (back of curb).

9.	Proposed profile of centerlines. Profile of flow lines of curb may be required

by the City Engineer.

10.	Stations, lengths, and elevations of vertical curve P.C., P.I., and P.T.

11.	Percent slope of tangent lines.

12.	Limits of construction.

13.	Show sufficient existing or future construction to assure continuity of

construction.

14.	Stations, cross sections, and elevations of drainage facilities and other

structures.

15.	Street light and underground service cable locations.

16.	Complete material list.

17.	High point, low point, K factor for curve.

18.	Street signage and pavement marking plan.

19.	Intersection detail drawings may be required by City Engineer.

(h)	Park Construction Plan Procedures and Requirements

In addition to the above general plan and profile details, all park construction

plans shall include the following:

1.	Landscape Plans

a.  Existing and proposed (design) contours maximum of two-foot intervals.

b.  Scale 1"=100' maximum with 1"=20' preferred.

c.  Existing plant material, if applicable, noting material to be saved and

methods of protection. For trees of four inch or larger caliper, indicate

size and species.

d.  Plant material schedule indicating common name and botanical name

including; genus, species, variety or cultivar, size and quantity.

e.  Proposed plant material shown at 2/3 mature size.

f.  All miscellaneous improvements and appurtenances including sidewalks,

drives, curbs, manholes, parking lots, etc.

g.  Graphic representation of all groundcover types, (sod, seed, bedding

plants, mulch, rock, etc.).

h.  Designation of all slope areas 4:1 or steeper.

i.  All proposed retaining walls or slope retention methods for slopes steeper

than 4:1.

j.  Seed mix and application rate for all seeded areas.

2.	Irrigation Plans

a.  It is the designers responsibility to prepare plans that are clearly

legible. Plans that are not legible shall be redrawn and resubmitted.

b.  Show existing irrigation, graphically distinguished from proposed

irrigation.

c.  All plans shall indicate all improvements or site conditions that shall

materially affect the successful operation of the system, such as

buildings, sidewalks, slopes, swales, plant groupings, ditches, etc.

d.  Show point of connection and size of water supply line.

e.  Show irrigation material schedule including pipe type and size, head type,

arc and nozzle, valve type and size, etc.

f.  Show Design Operating Pressure (D.O.P.) chart.

g.  Show trench depth schedule from top of pipe.

h.  Show standard City meter detail.

i.  Show backflow prevention detail.

j.  Label size of all pipe on plan.

k.  Give indication of each zone valve of zone number, valve size and gpm.

l.  Show all miscellaneous details required to construct the system.

3.	Recreational Facilities Plans

a.  All recreation athletic facilities (such as softball, baseball, soccer,

football, tennis and playground equipment) shall be reviewed on a case by

case basis and be approved by the City prior to beginning any construction

on the site. At a minimum, all such facilities plans shall meet the

requirements of these Standards and Specifications.

b.  A high level of detail may be required to determine the adequacy of

grading, layout requirements and building construction techniques.

108	SPECIFICATIONS AND SUPPORT DOCUMENTATION

The following items shall also be included with submitted construction plans:

1.	Reference on plans to City Standards and Specifications.

2.	Reference on plans to other agency Standards and Specifications that are required or

proposed.

3.	Where reference to other commonly available Standards and Specifications shall not

suffice, copies of specifications are to be provided.

4.	Copies of written approval from other affected agencies as required.

5.	Soils and other test data and design calculations for street structural sections,

drainage facilities and other appurtenances as required.

109	"AS-BUILT" DRAWINGS REQUIREMENTS

109.1	Certification Statement

It is the duty of the Responsible Party to record and document the physical dimensions

and any changes on a set of "As-Built" drawings and to certify as to their accuracy.

Certification Statement:

"These drawings are a correct "Record-Drawing" of the final construction of

improvements shown on these plans, as per subsection 109 of the Standards and

Specifications for the City of Scottsbluff."

DATE

109.2	"Record-Drawing" Information

The Responsible Party shall document the following information to certify the

construction plans as "Record-Drawing".

(a)	Streets

1.  Elevation check at a maximum 150 feet intervals in each flowline top of

curb along street, at the PCR of each radii, and flowline at the center of

each cross pan.

2.  Elevation at flowline at each side of storm inlets.

3.  Elevations at all points shown on the Cul-De-Sac detail, and at the center

and high points in the flowline.

(b)	Sanitary and Storm Sewers

1.  Elevation, size and material of all in and out inverts at manholes, inlets,

and outlets.

2.  Pipe lengths, pipe diameters, and stationing from manholes. All sanitary

sewer service connection location information is to be supplied by

contractor to the Responsible Party.

3.  Rim elevations on all manholes and drainage inlet structures.

4.  Elevation check every 100 feet in the thalweg of all drainage channels,

including elevation at all drop structures.

5.  Final detention pond volume from cross sections and the final release

rates per drainage criteria.

(c)	Water Mains

1.  Elevation of top of the water valve operating nut.

2.  Horizontal verification of water valves, tee's, cross's, fire hydrants,

and meter pits, type of material.

3.  Size, restraint area, and type of all thrust blocks, type of material

information to be supplied by contractor to the Responsible Party.

4.  The location of all service connections along the main.

(d)	Parks Improvements

1.  Redraw to accurate scale of 1"=20'. Noted dimensions on construction

drawings shall not be accepted.

2.  List of all plant material installed including size and quantities.

3.  Vertical and horizontal verification of all sidewalks and bike paths.

4.  Verification of all slopes shown on the construction plans.

5.  Horizontal verification of all physical features, including trees, back

stops, goals, lights, playground equipment, permanent benches or bleachers,

water fountains, public restrooms, fences, bike racks, etc.

6.  Irrigation as-builts shall include horizontal verification of all

irrigation pipes, irrigation heads, valve boxes, wiring (24 volt and 110

volt), electrical boxes, controller, and backflow protection device.

Noted information shall include all pipe size, zone number, valve location,

head type, valve type and model number, controller type and model number,

D.O.P. chart, and drip emitter chart. Irrigation as-builts shall show

pertinent physical features (such as sidewalks, fences, ponds, buildings,

parking lots and athletic fields). No contour lines shall be shown on

irrigation as-builts unless required by the City.

(e)	As-builts may be field verified by the City and shall be approved by the City

prior to initial acceptance by the City.

109.3	Submittal of Certified "As-Built" Plans and Documents

Once approved by the City, the Land Surveyor, Professional Engineer, Landscape

Architect or Architect shall submit two full size "As-Built" plans certified as

stated in subsection 109.1 and 109.2. The Land Surveyor and or Professional Engineer

shall also submit survey data taken to verify items listed in subsection 109.2.

SECTION 200

WATER SYSTEM STANDARDS

SECTION 200 - WATER SYSTEM STANDARDS

TABLE OF CONTENTS		                     				PAGE

201	GENERAL PROVISIONS	                     				200-1

202	GENERAL SPECIFICATIONS	                     				200-1

202.1	Granting of Service	                     			200-1

202.2	Permits	        	                     			200-1

202.3	Application Procedure	                     			200-1

202.4	Construction Procedure	                     			200-1

202.5	Acceptance of Work	                     			200-3

203	WATER DISTRIBUTION SYSTEM DESIGN CRITERIA	                     	200-4

203.1	General	  	                     				200-4

203.2	Quality of the Distribution System	                     	200-4

203.3	Demand Factors/Allowed Flows	                     		200-4

203.4	Sizing of Distribution Mains	                     		200-4

203.5	Materials		                     			200-5

203.6	Ground Cover	                     				200-5

203.7	Location		                     			200-5

203.8	Valves		                     				200-6

203.9	Blowoff Valves	                     				200-7

203.10	Fire Hydrants	                     				200-7

203.11	Thrust Blocks	                     				200-7

203.12	Operating Pressures	                     			200-7

203.13	Pressure Regulating Stations	                     		200-8

204	WATER DISTRIBUTION SYSTEM CONSTRUCTION SPECIFICATIONS           	200-8

204.1	Materials		                     			200-8

204.2	Corrosion Protection	                     			200-17

204.3	Excavation	                     				200-18

204.4	De-watering	                     				200-18

204.5	Pipe Bedding	                     				200-19

204.6	Installation of Pipe	                     			200-19

204.7	Installation of Valves and Valve Boxes                   	200-20

204.8	Testing		                     				200-20

204.9	Backfill		                     			200-20

204.10	Compaction	                     				200-21

204.11	Trench Maintenance	                     			200-21

204.12	Repair Fittings	                     			200-21

205	WATER SERVICE LINES AND APPURTENANCES

CONSTRUCTION SPECIFICATIONS	                     			200-22

205.1	General		                     				200-22

205.2	Materials		                     			200-22

205.3	Excavation	                     				200-23

205.4	De-watering	                     				200-23

205.5	Pipe Bedding	                     				200-23

205.6	Installation of Pipe	                     			200-23

205.7	Installation of Valves and Valve Boxes                   	200-23

205.8	Testing		                     				200-23

205.9	Backfill		                     			200-23

205.10	Compaction	                     				200-23

205.11	Location		                     			200-23

205.12	Depth		                     				200-24

205.13	Separate Trenches	                     			200-24

205.14	Connections	                     				200-24

205.15	Pumps		                     				200-25

205.16	Lawn Sprinklers	                     			200-25

205.17	Abandonment	                     				200-25

206	WATER MAIN RELEASE PROCEDURE	                     			200-25

206.1	Scope		                     				200-25

206.2	New Mains		                     			200-25

206.3	Repaired Mains	                     				200-26

206.4	Disinfection	                     				200-26

206.5	Flushing		                     			200-26

206.6	Hydrostatic Testing	                     			200-26

206.7	Bacteriological Sampling	                     		200-27

207	WATER METER INSTALLATION STANDARD SPECIFICATIONS                	200-27

207.1	General Information	                     			200-27

208	CROSS CONNECTIONS	                     				200-28

208.1	Definition	                     				200-28

208.2	Types of Cross Connection Control Devices                	200-28

208.3	Mandatory Backflow Prevention Installations              	200-32

208.4	Approved Backflow Prevention Devices                     	200-32

DETAIL DRAWINGS

200-1	  Typical Intersection Detail

200-2	  House Service Detail

200-3	  Bedding and Fire Hydrant Assembly Detail

200-6	  2" Blowoff Detail

200-6A	  Standard P.R.V. Installation Detail

200-7	  Standard P.R.V. Installation Detail

200-8	  Sump Pump Discharge Line Detail

200-9	  Air Relief Valve Assembly Detail

200-10	  Air Relief Valve Assembly Manhole Detail

200-11A  Waterline Lowering Detail

200-11B  Waterline Lowering Detail

200-14A  Standard 1-1/2" and 2" Meter Setting Detail

200-15A  Standard 3" and 4" Meter Setting Detail

200-16	  Standard Installation for Sprinkler Meter Detail: 1-1/2" and 2" Only

200-17A  Standard Installation for Sprinkler Meter Setting Detail: 3" and 4"

SECTION 200 - WATER SYSTEM STANDARDS

201	GENERAL PROVISIONS

These standards are promulgated by the Water Superintendent of the City of Scottsbluff.

Interpretation, enforcement and revision of these standards is delegated to the City Engineer.

202	GENERAL SPECIFICATIONS

202.1	Granting of Service

Water and sewer services shall be extended at the requester's expense, when it has been

determined that the City has the capability and capacity to serve the area, provided that

the area to be served is located within the City of Scottsbluff Water Service Area, and

provided that the applicant can show evidence of fee ownership of the property to be

serviced. The request for service must be in compliance with stipulations contained in

all utilities agreements entered into by the City and said applicant, as well as in

compliance with all applicable City Ordinances, Codes and the rules and regulations of

the State of Nebraska.

202.2	Permits

Permits shall be required for the construction of any water and sanitary sewer facility.

Permits shall be obtained from the City before any work is begun, and such permits shall

only be issued to Responsible Parties licensed and bonded in the City. No work relating

to water and/or sanitary sewer utilities performed outside the city limits of

Scottsbluff, yet still in the Scottsbluff Service Area, shall commence until the

appropriate entities have been notified and the necessary permits purchased. All permits

relating to any work involving the City utilities system must be approved by the City

Engineer prior to issuance.

202.3	Application Procedure

The City shall establish and amend from time to time procedures to be followed by

Responsible Parties performing work on water and/or sanitary sewer utilities. These

procedures shall include all requirements for documentation, submittals, fees,

engineering design, construction and acceptance. All drawings submitted must adhere to

acceptable drafting standards as established by the City. Plans shall be submitted to

the City Engineer as described in subsection 107.

202.4	Construction Procedure

Following final approval of the plans, the Responsible Party may proceed with

construction. In addition to all construction requirements contained in other portions

of these Standards and Specifications, the Responsible Party shall observe the

following:

(a)	Prior to the beginning of work a preconstruction conference shall be held between

The City, the Responsible Party who is scheduled to perform the work, the

designated on-site field representative, the consulting engineer and any other

entities involved in the construction.

(b)	Development phasing of any project must be shown on the construction plans and made

a part of the application procedure. No phasing shall be permitted unless this

requirement has been adhered to.

(c)	The work shall be surveyed and staked under the supervision of a licensed land

surveyor or Professional Engineer in accordance with the approved plans.

(d)	Construction shall adhere to the following sequence unless otherwise specified by

the City Engineer: Sanitary sewer line installation, curb and gutter installation,

water line installation. Under certain conditions, curb and gutter installation may

occur after water main installation; however, only upon approval of and under the

direction of the Inspector. Installation of water lines shall not be permitted

until all compaction results for sanitary sewer lines have been submitted to and

approved by the City, all minimum slopes for sanitary sewer installations have been

verified, and all applicable testing procedures have been conducted and approved in

writing.

(e)	Mains shall be chlorinated and hydrostatically tested in accordance with NDH

requirements.

(f)	All work relating to water and sanitary sewer utilities shall be inspected by the

City. Water mains shall be tapped only after having been installed to the

satisfaction of the Inspector, chlorinated, pressure and clearwater tested and

approved by the City. Service lines, from the main to the property line must be

installed prior to tapping. Taps for sprinkler systems and domestic systems larger

than two inches shall not be performed until the meter has been installed. No

tapping of dry mains shall be made or allowed.

(g)	No work shall begin until the installing Responsible Party is in possession of an

approved set of plans and Standards and Specifications. The City Engineer's

approval shall be for general conformity to the Utility specifications and shall

not constitute blanket approval of all dimensions, quantities and details of the

material or equipment shown. Nor shall such approval relieve the Responsible Party

or consulting engineer of his responsibility for errors contained in the drawings.

(h)	Paving shall not be permitted until manholes and valve boxes have been verified in

the field through a pre-paving walk through and minimum slopes on all sanitary sewer

lines have been verified.

(i)	Installation of all new facilities in the City's Service Area shall be inspected and

approved by the City.

(j)	The Inspector shall see that the materials furnished and the work performed are in

accordance with the plans and specifications approved by the City. The Responsible

Party shall furnish all reasonable aid and assistance required by the City Engineer

or Inspector for the proper examination of the materials and work. All work shall be

performed in accordance with accepted workmanship practices and these engineering

standards. Any work not accepted by the Inspector shall be redone until compliance

with these standards is achieved. Instructions given by the Inspector relating to

quality of materials and workmanship must be obeyed at once by the Responsible Party

The Inspector shall not supervise, set out work, or give line and grade stakes.

All materials used shall be new and subject to the inspection and approval of the

Inspector at all times. The Inspector has the right to perform any testing deemed

necessary to ensure compliance of the material of these standards. No material shall

be used before being inspected and approved by the Inspector. Failure or neglect on

the part of the Inspector to condemn or reject inferior materials or work shall not

be construed to imply their acceptance should their inferiority become evident at

any time prior to final acceptance of the work. Inspectors have the authority to

reject defective or inferior materials and/or defective workmanship and to suspend

work until such time as the Responsible Party shall correct the discrepancies in

question.

Whenever defective materials and work are rejected, the Responsible Party shall

promptly remove such defective materials and construction from the job site and

replace all defective portions to the satisfaction of the City Engineer or his

representative. In the event the Responsible Party fails to remove rejected items

from the job site within a reasonable length of time, the City Engineer may arrange

for such removal at the expense of the Responsible Party.

Inspection shall not relieve the Responsible Party from any obligation to perform

the work strictly in accordance with the plans and specifications or any

modifications thereof. Work not so constructed shall be removed and corrected by

the Responsible Party at his sole expense, whenever so ordered by the City

Engineer, without reference to any previous error or oversight in inspection.

(k)	Except in cases of emergency, maintenance or protection of work already completed,

no work shall be allowed between the hours of 5:00 p.m. and 8:00 a.m. nor on

Saturday, Sunday or legal holidays unless approved by the City Engineer in each

case. All requests for overtime shall be made to the City Engineer

at least 48 hours in advance.

(l)	In the event one or more inspectors representing private consulting engineering

firms are also inspecting a project, along with the City's Inspector, the

instructions given by the City Engineer shall prevail in the event of conflicting

instructions.

202.5	Acceptance of Work

Water and Sewer utilities shall be inspected throughout installation. Upon completion of

installation and prior to paving operations, a punch list shall be formulated stating all

discrepancies that relate to water and sewer utilities. This punch list, made by the

Inspector, shall be submitted to the Responsible Party. Any work requiring the cutting of

the street shall be done at this time. At this time, the Responsible Party shall also

check and ensure that all water and sewer services are offset from the centerline of each

lot by five feet each side unless otherwise indicated on the engineering drawings. No

services are to be located in concrete areas.

After paving operations (all lifts) have been completed, a second punch list shall be

formulated and sent to the Responsible Party. Once this punch list has been completed,

and the deeds, as well as cost estimate and "As-Built" drawings for all utility lines

have been submitted to the Division, the one year warranty period shall begin.

203	WATER DISTRIBUTION SYSTEM DESIGN CRITERIA

203.1	General

All water mains and appurtenances shall be in conformance with these Standards and

Specifications and shall be designed by or under the direct supervision of the

registered professional engineer licensed to practice in the State of Nebraska.

203.2	Quality of the Distribution System

the purpose of these Standards and Specifications is to ensure that only proven high

quality materials are installed with first class workmanship. Determination of the best

materials and construction methods are based upon lowest life cycle costs, not

necessarily upon lowest initial costs. the sizing and layout of the system are part of

the total consideration of design, operations and maintenance of a water supply system

that yields optimum quality service at the lowest total cost to the consumer.

203.3	Demand Factors/Allowed Flows

Water mains shall be designed to supply projected demands of the proposed development.

The following water flow parameters shall be guidelines to determine estimated flows:

Max. Month     Max. Day     Max. Hr.

DEMAND FACTORS                        Avg. Day       Avg. Day     Avg. Day

Residential                           1.8            3.2          5.76

Office/Commercial/Industrial          1.1            1.8          3.24

Overall System                        1.8            2.6          4.68

125-150 gallons/person/day is standard.

All water mains shall be designed using velocities of not more than five feet per second

for the maximum hour. (Fire flow shall not exceed seven feet per second)

All calculations of flows to be used by the proposed project are to be submitted to the

City for review, along with the engineering drawings.

203.4	Sizing of Distribution Mains

The minimum diameter for water mains in residential areas, excluding cul-de-sacs, shall

be six inches. All schools, shopping centers, business parks, industrial parks and high

density residential areas shall be looped with mains at least eight inches in diameter.

Six inch diameter pipe may not be used in stretches of more than 600 feet in length

unless approved by the City Engineer. All water lines shall be looped. No dead-end lines

shall be permitted, unless specifically approved by the City Engineer. Upon approval by

the City Engineer, six inch water lines may extend into cul-de-sacs serving not more

than ten single family residential units and not be looped. All six inch lines shall be

either ductile iron pipe or polyvinyl chloride pipe as specified in subsection 204.01.

In no case shall a line of less than six inches in diameter be used to serve a fire

hydrant. Water lines in cul-de-sacs of more than ten residential units must be looped.

The maximum acceptable head loss shall be two feet per 1,000 feet of main. The City

Engineer reserves the right to size mains to provide service for future needs. No

service line taps shall be permitted to transmission lines unless specifically approved

by the City Engineer. Water main sizing shall be in conformance with the current water

system master plan. Sizing of on-site mains shall be accomplished by utilizing a flow

network model incorporating any one of the several acceptable flow network analysis

methods, such as the Hardy Cross. Results shall be submitted to the City Engineer,

along with the engineering drawings.

Oversizing of mains (anything greater than 6 inches in size) may be required by the City.

Reimbursement agreements may be entered into so that the Responsible Party may recover up

to 50 percent of the costs incurred for the first 6 inches of pipe diameter.

203.5	Materials

Only water mains constructed of the following materials shall be allowed: ductile iron

pipe (DIP) or polyvinyl chloride pipe (PVC).

All materials must conform with the material requirements as set forth in subsection

204.1 of these Standards and Specifications.

Transmission lines (12 inches and larger) shall be ductile iron pipe. Design calculations

on pipe wall thickness and strength must be submitted for approval along

with the construction drawings.

203.6	Ground Cover

All mains shall be designed as required by NDH. Through areas where future roadways may

exist, design of the line needs to be coordinated with the City Engineer to prevent

situations of lowerings or risings as a result of future road profiles.

When a water main crosses underneath a stream, irrigation ditch, storm drainage ditch or

other area which has surface water for a significant period of the year, steel casing

pipe and corrosion protection shall be required. In all cases, valves are to be located

in such a manner that the water main at such crossings can be completely isolated.

203.7	Location

All mains shall be installed in dedicated streets. Location for these water mains, where

practicable, shall be behind the proposed curb on the north or west side of the street.

In addition, a minimum separation of five feet from the lip of pan or edge of pavement is

required for the water main, unless otherwise specified by the City Engineer.

Water mains shall be installed in exclusive easements, either by plat or separate

document satisfactory to the City Engineer, when, as determined by the City Engineer, it

is not practical to make such installation in the dedicated street. Under no

circumstances shall any structures be constructed within these easements or right-of-

way without prior approval, including terms and conditions, as set by the City. The

minimum width requirements for water easements are twenty feet, with the pipeline

centered in the easement and offset five feet from any property line. In the event two

utility lines share the same easement, the minimum width for the easement shall be

thirty feet.

All water mains shall be in an easement of a width at least two times the depth to the

invert unless otherwise specified by the City Engineer. Valves shall be located at each

end of the easement in order to isolate that portion of the line if necessary.

Water line installations shall conform to all specifications as described in the

regulations adopted by the State of Nebraska Department of Health, "Guidelines for Water

System Design".

203.8	Valves

Residential distribution systems shall be valved in such a manner as to ensure that no

more than 600 feet of main or 18 residential units may be out of service for any one

single break. Commercial and other distribution systems shall be valved in such a manner

as to ensure that no more than 300 feet of main may be out of service for any one single

break.

Valve placement shall be such that there are at least two valves at every tee and three

valves at every cross. Valves are required between all fire hydrants. Valves shall be

no further than 1,200 feet apart on transmission line (16 inches and larger).

When water mains are designed in such a way that a dead-end exists at the edge of a

subdivision or at the boundary of a filing within a subdivision, the main shall be

terminated with a temporary blowoff valve. Where future connections are to be made to

temporary dead-ends, at least three lengths of pipe are required beyond the valve and

before the temporary blowoff valve. When a new extension shall connect to an existing

main not terminated with a valve, the new main must be valved at the connection in order

that the entire, newly constructed system, may be pressure tested and chlorinated.

Valves larger than 10 inches shall be butterfly style. All valves exceeding a depth of

five feet shall be furnished with a valve key extension operating rod extending to within

four feet of the top of the valve box.

Whenever possible, main line valves shall be located at a point on the main which is

intersected by an extension of the property line. Under no circumstances, however, shall

a valve be located in concrete areas, such as sidewalks, cross pans, aprons, curbs or

gutters. Valves located on water lines utilizing easements shall be located a distance

of three feet, three inches from connecting tees, cross or elbow in pavement areas and

not on property lines. Butterfly valve operators shall be located on the north or east

side of the water main. Any valve located in a green belt area shall have a concrete

collar around the valve box or manhole as shown in the detailed drawings.

203.9	Blowoff Valves

Blowoffs are required at the end of water mains which terminate at the subdivision

boundary in streets that shall be extended at a future date. Blowoffs are also required

at all low points in transmission lines (16 inches and larger).

Blowoff assemblies consist of valves, pipe and material necessary to install the

blowoff valve complete in place. Where specified by the City Engineer, blowoffs shall

be required at the end of mains extended into cul-de-sacs.

203.10	Fire Hydrants

Maximum distance between hydrants shall be 500 feet in single family and duplex

residential areas, and a minimum spacing to cover all of the area within a 300 foot

radius from the hydrant in business and high density residential areas, such

as apartments and townhouses. The maximum distance should be measured along the

centerline of the street, unless approved otherwise by the City Engineer. No hydrants

shall be allowed at the end of cul-de-sacs. the number and location of fire hydrants in

a given area shall be determined by the local fire department. If hydrants are to be

installed at locations other than street intersections, they shall be located on lines

which are established by extending property lot side lines into the streets. The fire

hydrant shall be located within the right-of-way and on the same side of the street as

the water main unless otherwise specified by the City Engineer. Installation of fences

or other obstructions shall in no way hinder the operation of the fire hydrant.

Fire hydrant branch lines shall be set at 90 degrees to street mains. The maximum length

of a fire hydrant branch line shall be 50 feet. The hydrant shall be set at the end of

the branch lines and shall face the branch line. No horizontal bends or offsets shall be

used in installing fire hydrant branch lines. Under no circumstances shall any size or

manner of tap be made on a fire hydrant branch line. Hydrants shall be plumbed vertically

with pumper nozzle facing street and traffic safety flange not less than two inches nor

more than three inches above final grade. A six-inch gate valve shall be flanged or

rodded to the tee on the main in order that the hydrant may be removed from the system

for maintenance without affecting the distribution system. No service line taps shall be

made to a distribution main within five feet of a fire hydrant branch line.

203.11	Thrust Block

All bends, tees, plugs, dead-ends, wet taps, hydrants, and blowoffs shall be designed and

constructed with concrete thrust blocks as set forth in subsection 204.1(1) of these

Standards and Specifications.

203.12	Operating Pressures

Pressures within the distribution system shall be a minimum of 40 pounds per square inch

(psi) during the maximum hour demand. Maximum pressure within the distribution system

shall be 100 psi. Pumping facilities shall be allowed on mains or service lines only

where specifically authorized by the City Engineer.

203.13	Pressure Regulating Stations

Pressure reducing valve (PRV) installations are used to control pressures between

distribution zones. When main extension plans are submitted for review, the need for a

pressure regulating valve installation shall be determined based on existing pressure

zones and the existing distribution system. Plans shall be submitted indicating size,

type and location for the PRV installation. All calculations must be submitted and

approved by the City. Drawings with all fittings shown must be submitted with

shop drawings for the vault prior to construction.

Individual PRV installations on residential services shall not be permitted, unless

specifically approved by the City Engineer.

204	WATER DISTRIBUTION SYSTEM CONSTRUCTION SPECIFICATIONS

204.1	Materials

All materials furnished shall be new and undamaged. Everything necessary to complete all

installations shall be furnished and installed whether shown on approved drawings or

not, and all installations shall be completed as fully operational.

Acceptance of materials or the waiving of inspection thereof shall in no way relieve the

Responsible Party of the responsibility for furnishing materials meetings the

requirements of the specifications.

The City reserves the right to direct or deny use of certain types of materials in

specific circumstances. All materials delivered to the job site shall be adequately

housed and protected so as to ensure the preservation of their quality and fitness for

the work.

(a)	Ductile Iron Pipe

All ductile iron pipe shall be manufactured in accordance with AWWA Standard C-150

and C-151, "Ductile Iron Pipe; Centrifugally Cast in Metal Molds or Sandlined Molds

for Water or Other Liquids," with the following additional requirements or

exceptions.

"Push-on single gasket" type conforming with applicable requirements of AWWA

Standard C-111. "Rubber Gasket Joints for Cast-Iron and Ductile Iron Pressure Pipe

and Fittings." Joint types other than "push-on single gasket" are acceptable if

specifically approved by the City Engineer.

Ductile pipe furnished under this specification shall conform to AWWA C-150 and C-

151 and the following minimum thickness classes unless otherwise specified by the

City Engineer:

12-inch and smaller - Class 51

14-inch and larger - Class 50

Pipe furnished shall have nominal laying lengths of either 18 feet or 20 feet.

Random lengths are not acceptable.

Pipe furnished shall have standard thickness cement mortar linings in accordance

with AWWA Standard C-104, "Cement Mortar Lining for Cast-Iron and Ductile Iron Pipe

and Fittings for Water," and the exterior coating shall be the standard outside

bituminous coating as specified in AWWA C-151.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

Corrosion protection shall be covered in subsection 204.2 of these Standards and

Specifications.

In general, ductile iron water pipe shall installed per AWWA C-600.

(b)	Polyvinyl Chloride (PVC) Pressure Pipe

All polyvinyl pipe shall be manufactured in accordance with AWWA Standard C-900,

"Polyvinyl Chloride (PVC) Pressure Pipe," with the following additional

requirements or exceptions. All pressure Class 150 pipe shall meet the requirements

of DR-18 and pressure Class 200 shall meet the requirements of DR-14.

Solvent cement joints are strictly prohibited.

Each length of pipe shall be a standard laying length of 20 feet. Random lengths

shall not be acceptable unless specifically approved by the Engineer. Under no

circumstances shall the random length be less than 10 feet long, with the exception

of fire hydrant branch lines and fittings. All PVC pipe must be laid with tracer

wire (16 gauge wire only).

PVC must conform with cast-iron outside diameters. Pipe stored outside which may be

exposed to sunlight for more than 30 days, shall be covered with an opaque material

such as canvas. Clear plastic sheets shall not be used to cover the pipe. Air

circulation shall be provided under the covering. Sunburned pipe shall not be

permitted for installation and shall be removed from the job site immediately. All

pipe must be Underwriters Laboratory approved. No direct taps shall be permitted

on PVC pipe.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

(c)	Fittings

All cast-iron fittings shall be manufactured in accordance with the following AWWA

standards: C-104 "Cement Mortar Lining for Cast-Iron and Ductile Iron Pipe and

Fittings for Water," C-110 "Gray Iron and Ductile Iron Fittings" and C-111, "Rubber

Gasket Joints for Cast-Iron and Ductile Iron Pressure for Pipe and Fittings," with

the following additional requirements or exceptions:

All fittings shall be furnished with a cement mortar lining of standard thickness

as defined in referenced specifications and given a seal coat of bituminous

material.

All fittings shall be furnished with mechanical joint, ring-tile or flanged ends

conforming to referenced specifications and, in addition, the tee-head MJ bolts

and hexagon nuts shall be fabricated from a high strength, low alloy steel known

in the industry as "Cor-Ten" or approved equal. Swivel fittings as approved by

the City Engineer may also be utilized.

All fittings shall be of the 250 psi pressure rating and shall conform to the

dimensions and weights shown in the tables of referenced specifications. All

fittings shall be made from gray iron and ductile iron.

The manufacturer shall furnish a certified statement that the inspection and all

of the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

Corrosion protection shall be covered in subsection 204.2 of these Standards and

Specifications.

(d)	Gate Valves

All valves shall be manufactured and tested in accordance with AWWA C-509,

"Resilient-seated gate valves, three through 12 NPS, for Water and Sewage Systems"

with the following additional requirements or exceptions:

All valves shall be suitable for frequent operation, as well as service involving

long periods of inactivity. The operating pressure for all valves four inches

through 12 inches shall be 200 psi.

Valve stems shall be made of bronze and threaded so that valves shall open by

turning to the left (counterclockwise). Each valve shall be furnished with a two-

inch square operating nut. The operating nut shall have an arrow showing the

direction of opening and the word "OPEN" cast on the nut. The stem seal shall

consist of two O-rings; one or both positioned above the thrust collar with the

valve under pressure in the full open position.

Bolts and hex nuts used on the bonnet of the valve shall be the manufacturer's

standard fabricated from a low alloy steel for corrosion resistance.

The flat gaskets, either ring type or full faced type, required at the bonnet

connections shall be fabricated from compressed asbestos sheet with a rubber

compound binder.

Flanges shall be sized and drilled in accordance with ANSI B-16.1 Class 125

specifications. Flanges shall be machined in a flat face or machined to a flat

surface with a serrated finish in accordance with AWWA Standard C-207 "Steel

Pipe Flanges." (Non-bury applications only)

All components of the mechanical joint shall conform to ANSI A-21.11 (AWWA

Standard C-111). The tee-head bolts and hexagon nuts shall be fabricated from a

high strength, low alloy steel known in the industry as "Cor-Ten" or an approved

equal.

After approved factory assembly, each valve shall be given the operation and

hydrostatic tests in accordance with the referenced specifications.

Wedge disc valves shall be limited to the following manufacturers or approved

equivalent. Resilient-seated gate valves shall be limited to Mueller Resilient Seat

Gate Valve No. A-2370 or Clow Resilient Seat Gate Valve.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

Corrosion protection shall be covered in subsection 204.2 of these Standards and

Specifications.

(e)	Valve Boxes

Valve box parts shall be Tyler, Clow or an approved equivalent manufacturer and made

of gray cast-iron. A 5-1/4 inch screw-type shaft shall be adjustable from 45 to 66

inches. Valve box lids shall be marked with the word "WATER" and shall have a lip or

flange extending into the valve box shaft. No slip-type boxes shall be allowed. The

valve box shall be of a design which shall not transmit shock or stress to the valve

and shall be centered and plumb over the operating nut of the valve with the box

cover flush with the surface of the pavement. In non-paved areas, a 24-inch square

concrete collar is required around valve box cover as per the standard detail in

Section 200 of these Standards and Specifications. In unimproved roadways the valve

box cover shall be set six inches below final grade with a marker post indicating

the location as per the standard detail drawing.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

Corrosion protection shall be covered in subsection 204.2 of these Standards and

Specifications.

(f)	Butterfly Valves

All valves 12 inches or larger shall be butterfly valves, Class 150B, and shall

conform to Specification AWWA C-504. All butterfly valves shall shall be furnished

with flanged end (non-bury applications) or mechanical joint connections and shall

be suitable for buried service installation. Butterfly valves used for buried

service shall be similar to the "Groundhog" manufactured by the Henry Pratt Company,

M & H 450 or an approved equal. Shafts shall be a one piece unit constructed of

stainless steel and shall extend completely through the valve disc body. Shaft

bearing material shall have a proven record of service of not less than five years.

Shaft seals may be designed for the use of standard split-V type packing or for

standard "O" ring seals. Valves shall be fitted with a two-inch operating nut and

shall open to the left (counterclockwise). All butterfly valves shall be designed

for direct bury unless otherwise designated. Valves shall be supported after

installation by a poured in place concrete pad with a bond breaker material.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

Corrosion protection shall be covered in subsection 204.2 on these Standards and

Specifications.

(g)	Pressure Reducing and Regulating Valves (PRV's)

All pressure reducing valves shall be Clayton 90-01 series or an approved

equivalent, unless otherwise approved by the City Engineer. The valve shall be

designed to reduce a high upstream pressure to a constant downstream pressure by

way of a pilot control system. The pilot system shall control the main valve which

shall be of a single seated, hydraulically operated, diaphragm, globe valve type.

The valve seats shall be bronze except when due to sustained high velocities

through the valve, the manufacturer recommends stainless steel seats. An indicator

rod or flow tube shall be furnished as an integral part of the valve to show the

position of the valve.

Material shall be cast-iron for valve body. Flanges and covers shall conform to ASTM

Standard Designation A-48. Bronze castings or parts for internal trim shall conform

to ASTM Standard B-61.

All valves shall be furnished with flanged ends and drilled in accordance with ANSI

B-16.1 Class 125 specifications. Flanges shall be machined to a flat face or

machined to a flat surface with a serrated finish in accordance with AWWA Standard

C-207.

The pilot valve for controlling operation of the main valve shall be a single

seated, diaphragm operated and spring loaded type. The pilot valve shall be attached

to the main valve with piping and isolation valves so arranged for easy access in

making adjustments and also for its removal from the main valve while the main

valve is under pressure. Pilot control system shall be cast bronzed ASTM B-62 with

303 stainless steel trim.

The needle valve shall be all bronze and included with the main valve to control

the speed of piston travel.

The operating pressure shall be 150 psi.

The body of the pressure reducing valve shall be given a hydrostatic test of 50

percent more than the operating pressure specified herein. A second test to

check seating of the cylinder shall be made at the operating pressure.

All pressure reducing and regulating valves shall be installed in concrete

vaults or factory built steel vaults as specified in the detail drawing. There

shall be no dissimilar metals allowed in the piping in the PRV vaults without

proper insulation.

The manufacturer shall furnish a certified statement that the inspection and all

of the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

After approved factory assembly, each valve shall be given the operation and

hydrostatic tests in accordance with the referenced specifications.

The manufacturer shall furnish a certified statement that the inspection and all

of the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

(h)	Air Valves

Air Valves shall be of two types as follows:

1.	An Air Valve called for on the plans shall mean an Air and Vacuum Valve of the

ball type designed to permit the escape of air from a pipe line when the line

is being filled and to permit air to enter the pipe line when the line is

being emptied.

2.	A Combination Air Valve called for on the plans shall mean a combination Air

and Vacuum and Air Release Valve designed to fulfill the functions of an Air

and Vacuum valve and also designed to permit the escape of air accumulated in

the line at the high point when the line is under pressure while in operation.

The valve shall be self-contained in one unit, not a combination of two valves.

This type would normally only be used in large transmission mains with few

connections.

Air valves shall be installed at each highpoint in all water mains of 12-

inch diameter and larger. One-inch air valves shall be installed on six-inch

and eight-inch mains at high points. Installation shall include gate valves

between saddle and air valve for maintenance purposes. They shall be installed

in precast concrete manholes or vaults as specified in Subsection J and fitted

with air vents of adequate cross section open to the atmosphere. A minimum

section one foot thick of 1 1/2-inch rock shall be placed under the pipe in air

valve manholes. When air valves are required, specifications shall be submitted

to the City Engineer for review and approval. These specifications shall

include the size, type, and all calculations required.

(i)	Blowoff Assemblies

Blowoff assemblies or drain valves shall be installed at each low point in all water

mains of 12-inch diameter and larger. All water mains installed having dead-ends

where stagnant water may collect shall be provided with blowoff devices which shall

allow flushing of the main without interruption of water service. Refer to blowoff

assembly detail for water mains less than 12 inches in diameter. All water mains of

12-inch diameter and larger shall use fire hydrants for blowoff assemblies, unless

otherwise specified by the City Engineer.

(j)	Vaults

All valve vaults shall be designed to adequately house the valves and fittings

therein contained, as well as to withstand all external loadings imposed by earth,

thrust and AASHTO H-20 highway live loading. Vaults located in areas other than

those that shall involve vehicular traffic may be designed for a loading other than

AASHTO H-20 by a professional engineer registered in the State of Nebraska.

1.	All concrete vaults shall be furnished with removable roof slabs to allow

removal of all valves and fittings. They shall also be sized so as to allow

sufficient room for valve maintenance and minor repair. Vault shall be

equipped with a prefabricated rectangular metal access door reinforced for

H-20 traffic loading. The access door shall be provided with a hinged 1/4-

inch x two-inch steel strap locking device.

2.	An all aluminum access ladder shall be provided. The ladder shall meet UL

and OSHA approval under Type I, Heavy Duty Specifications.

Vaults shall be constructed in such a manner as to allow operation of all valves

from above ground and shall be fitted with air vents open to the atmosphere. Vaults

shall be made waterproof after construction by use of sealants, epoxies or other

approved methods. All vaults shall be designed with wall sleeves and link seal and

be capable of handling thrusts caused by operating valves. If the vault is not to

be in a street, the roof shall be designed to support the overhead earth fill and

any other reasonable loading that may occur. All vaults shall have 110/120 volt,

water tight outlets and light fixtures. The light switch shall also be connected to

the vent fan and be located in such a position that it can be operated without

completely entering the vault. The vault shall also be equipped with a sump pump and

ventilation fan meeting the following specifications:

1.	Sump pumps shall be bronze mounted with automatic float controls by Hydro-

matic with a 1/3-H.P. motor designed to operate with 120 volts, or an approved

equivalent. A pipe union shall be installed in the discharge line between the

pump and the check valve to aid in the removal of the pump for repair or

replacement.

2.	Ventilation fans shall be as manufactured by ILG, or an approved equivalent,

Model PTD Direct-Drive Tubeaxial Duct Fan size PTD 123 (811 cfm @ 3/8" s.p.)

with a 1/6-H.P., 120-volt constant speed, single phase, 60HZ electric motor.

Control switch for the fan shall be mounted next to the entryway so that it can

be operated without completely entering the vault. The discharge of the vent

fan shall be totally enclosed and attached to the opening of the exhaust vent

pipe.

Concrete floors shall have 12-inch diameter by 18-inch deep sump holes in the corner

but not open to the outside of the vault. The designing engineer shall submit shop

drawings along with design calculations including the electric layout to the City

Engineer for approval prior to the installation. Refer to the detail drawings.

(k)	Precast Concrete Manholes

Refer to subsection 303.2(c) of these Standards and Specifications.

(l)	Thrust Blocks

Thrust blocks shall be constructed at all bends and fittings which result in

unbalanced line thrust. Care shall be taken not to block outlets or to cover bolts,

nuts, clamps or other fittings or to make them inaccessible. A bond breaker shall be

placed between the fitting and the thrust block to aid in ease of future removal.

The vertical sides of the concrete thrust blocks shall be formed to allow for

symmetrical thrust. All concrete thrust blocks shall be designed for shape and size

as required by type of soil and shall in every instance bear against undisturbed

earth. If soil bearing strength is unknown, soil bearing capacities used in design

must be approved by the City Engineer. When it is impossible through over excavation

or other causes to pour a thrust block against undisturbed earth, harness rods shall

be required to anchor the fittings to the main upon approval of the City Engineer.

Backfill may be placed over the thrust block once the surface has set sufficiently

to resist the weight of the backfill. However, no tamping or compacting shall be

allowed above the thrust block for a minimum of 24 hours after placement. Concrete

must set a minimum of 48 hours prior to the performance of a hydrostatic test. NO

DRY KICKERS SHALL BE ALLOWED. Refer to the detail drawings.

(m)	Concrete

All cement used shall be Portland Cement acceptable under ASTM Designation C-150

"Standard Specifications and Tests for Portland Cement." Cement used shall be Type

I, II LS or Type IV. All concrete shall have a minimum 28-day compressive strength

of 4,000 psi. The design mix of Portland Cement, fine aggregate, course aggregate,

water and admixtures shall be submitted along with test results of the design to

the City Engineer for approval upon request. Hand mixed concrete shall not be

permitted.

Concrete shall not be placed on frozen subgrade. Concrete shall be placed only in

the presence of the Inspector unless inspection has been waived prior to the

placement. When concrete is deposited against ground without the use of forms, the

ground shall be thoroughly moistened or other provisions made to prevent the ground

from drawing water from the concrete. Newly placed concrete shall be allowed to set

undisturbed for a minimum curing time of 24 hours. When concrete is placed at

temperatures below 40 degrees F., the Responsible Party shall provide satisfactory

methods, as determined by the City Engineer, and means to protect the mix from

injury by freezing and comply with all American Concrete Institute (ACI) standards

(latest revision.) After placement of concrete, an eight-mil polyethylene covering

shall be required for 24 hours in order to allow for proper curing. No trucks shall

be permitted to place concrete, if placement does not begin prior to 90 minutes from

when the truck left the plant. Allowable slump shall be three inches, (+/-) one

inch.

(n)	Tie rods

Tie rods shall be mild steel, ASTM Standard Designation A-36. Hex nuts shall be

ASTM Standard Designation A-307, grade A or B, Hexagon Heavy series. Tie rods shall

be used at all bends and fittings where thrust blocks cannot be used due to existing

field conditions or where harness rods are specifically required by the City

Engineer. All harness rods shall have a bituminous coating for corrosion protection

as specified by the City Engineer.

(o)	Concrete Reinforcement

All deformed reinforcing bars shall conform to ASTM Standard A-615, Grade 40 or 60,

or ASTM Standard A-617, Grade 40 or 60. All welded steel wire fabric shall conform

to ASTM Standard A-185.

(p)	Galvanized Material

Under no circumstances shall any galvanized fittings or material be used unless

specifically approved by the City Engineer.

(q)	Fire Hydrants

All fire hydrants shall conform to and be tested in accordance with AWWA

Specification C-502. Fire hydrants shall be made of cast-iron with full bronze

mountings. Inlet shall fit six-inch pipe with barrel length sufficient for a 5-1/2

foot trench. Hydrants shall have one 4 1/2-inch pumper connection and two 2 1/2-

inch hose connections, and the main valve opening in the fire hydrant shall be

not less than five inches in diameter. Threads on all nozzles shall be National

Standard. All fire hydrants shall close clockwise.

A traffic breakaway feature shall be incorporated into the barrel of the hydrant at

the ground line. The operating nut shall be National Standard pentagon measuring

1-1/2 inches from point to opposite flat. Nozzle covers shall have the same size

and shape nut as the operating nut. The hydrant shoe shall have a mechanical joint

fitting with the tee-head bolt and hexagon nut made of Cor-Ten.

Each hydrant shall have drain holes with a minimum thickness of 12 inches of 3/4-

inch rock beneath them and 6-inches above. A sheet of four mil polyethylene should

be placed over the rock to prevent dirt from filling the rock. All hydrants shall

stand plumb and shall be connected to the street main by a six inch branch line. The

branch lines shall be PVC Class 150 or ductile iron pipe only. An independent six-

inch gate valve shall be installed on each fire hydrant branch, rodded to the tee.

Thrust blocks under and behind the fire hydrant base shall be placed according to

the fire hydrant detail. The fire hydrant base shall be above finished grade, when

finished grade has been established. All hydrant extensions needed to place hydrant

at correct grade shall be considered essential to the project and not a separate pay

item. Maximum height of extension on hydrant is 12 inches. No hydrant base shall be

installed any deeper than six feet from the top of finished grade. All fire hydrant

assemblies shall be rodded in accordance with subsection 204.1(n).

No part of the fire hydrant assembly shall protrude over the edge of sidewalks.

Minimum distance from driveways shall be five feet. Depending upon hydrant

location, the use of steel posts filled with concrete may be required for

protection, as specified by the City Engineer. Fire hydrants shall be placed on

property lines at corners or in the middle of the block in residential areas.

Commercials (Large tracts) may vary. All hydrants shall be located within the right-

of-way adjacent to public streets, unless otherwise determined by the City Engineer.

Corrosion protection shall be covered in subsection 204.2 of these Standards and

Specifications.

After hydrant installation is complete, the Responsible Party shall paint each

hydrant with Rustoleum Federal Safety Orange, or an approved equivalent. Fire

hydrants shall not be accepted nor shall the one year warranty period be initiated

until the hydrant color matches the existing City hydrant colors as specified by

the City Engineer.

Fire Hydrants shall be limited to the following manufacturers only.

Mueller Company 5-1/4 Centurion. Centurion model shall be connected with stainless

bolts and nuts where the show and barrel connect. (Federal Safety Orange.)

For additional information refer to fire hydrant detail drawing.

204.2	Corrosion Protection

All ductile iron pipe, steel casing pipe, fittings, valves and valve boxes shall be

protected as specified if the City Engineer determines the soils require corrosion

protection.

All ductile iron pipe, fittings, harness rods, valves and valve boxes shall be hand

wrapped using polyethylene with a minimum wall thickness of 8 mils and two-inch wide,

10-mil thick, polyethylene pressure sensitive tape to close seams or hold overlaps.

All polyethylene encasement material shall be manufactured in accordance with AWWA

Standard C-105. The raw material used to manufacture polyethylene film shall be Type I,

Class A, Grade E-1 in accordance with ASTM Standard Designation D-1248.

In all cases the polyethylene shall be so applied as to prevent the contact of backfill

material with the fitting.

Other means of corrosion protection must be specifically approved by the City Engineer.

The Responsible Party shall incur the costs of all soil testing if required.

204.3	Excavation

All excavations shall be made to the lines and grades as established by the approved

drawings in open cut, through whatever material encountered. All areas shall be excavated

in such a manner as shall afford adequate drainage. Where material encountered within the

limits of the work is considered unsuitable by the City Engineer, such material shall be

excavated below the grade shown on the drawings to a depth necessary to ensure a stable,

firm foundation and refilled with 3/4-inch rock uniformly graded to provide a firm

foundation. All excavated materials which are considered unsuitable and any surplus of

excavated material shall be disposed of by the Responsible Party.

All existing asphalt or concrete surfacing shall be cut vertically in a straight line as

specified in subsection 103.3 and removed from the job site prior to starting the trench

excavation. This material shall not be used in any fill or backfill.

The trench shall be excavated so that a minimum clearance of six inches is maintained on

each side of the pipe for proper placement and compaction of the bedding or backfill

material. The maximum trench width measured at the top of the pipe shall be the outside

diameter of pipe plus 24 inches.

If the trench width exceeds the maximum trench width, a stronger class pipe shall be

specified.

The trench shall be adequately supported and the safety of workers provided for as

required by the most recent standards adopted by OSHA.

If the City Engineer is of the opinion that at any point the trench walls are not

properly supported, the City Engineer may suggest the placement of additional supports

by and at the expense of the Responsible Party, and compliance with OSHA Standards is the

responsibility of the Responsible Party for the safety of all work being conducted. The

City is not responsible for the safety of any party constructing the utility project.

Trench excavation shall not advance more than 400 linear feet ahead of pipe laying and

backfilling work.

Excavation for structures shall be of such dimensions as to allow for the proper

installation and to permit the construction of the necessary pipe connections.

204.4	De-Watering

All pipe trenches or structure excavation shall be kept free from all water during pipe

laying and other related work. The method of de-watering shall provide for a completely

dry foundation at the final lines and grades of the excavation. All water shall be

disposed of in a suitable manner approved by the State Health Department without being

a menace to public health safety or causing a public inconvenience. The de-watering

operation shall continue until such time as it is safe to allow the water table to rise

in the excavations. Pipe trenches shall contain enough backfill to prevent pipe

flotation.

204.5	Pipe Bedding

After completion of the trench and proper preparation of the foundation, bell holes shall

be dug deep enough to provide a minimum of two inches of clearance between the bell and

the bedding material. All pipe shall be installed in such a manner as to ensure full

support of the pipe barrel over its entire length. After the pipe is adjusted for line

and grade and the joint is made, the bedding material shall be carefully placed and

tamped under the haunches of the pipe up to spring line and in the previously dug bell

holes. The bedding shall then be installed to a minimum of six inches and a maximum of 12

inches above the top of the pipe, no matter what type of pipe is being installed.

The bedding material shall be squeegee non-fractured and shall conform to the following

limits when tested by means of laboratory sieves:

Total Percent

Sieve Size                Passing by Weight

3/8-inch                  100

No. 200                   0-5

204.6	Installation of Pipe

All pipe shall be installed in accordance with AWWA C-600 or C-603 along with the

following provisions:

Pipe and fittings shall be loaded and unloaded by lifting so as to avoid shock or

damage. Under no circumstances shall such material be dropped. Before the placing of

pipe in the trench, each pipe or fitting shall be thoroughly cleaned of all foreign

material, kept clean at all times and examined for cracks or defects before installation.

Joint lubricant shall be as supplied by the pipe manufacturer.

When laying pipe on curves, the pipe shall be kept in alignment by deflecting joints.

When using deflecting joints, recommended practices and allowances as stipulated by the

manufacturer must be adhered to at all times. Pipe shall be laid with the bell ends

facing in the direction of laying unless directed otherwise by the City Engineer.

Whenever the pipe is left unattended, temporary plugs shall be installed at all openings.

Temporary plugs shall be watertight, Standard Cast-Iron and of such design as to prevent

children and animals from entering the pipe. All temporary plugs shall be approved by

the Inspector.

No pipe or appurtenant structure shall be installed upon a foundation into which frost

has penetrated or at any time when the Inspector deems there is a danger of ice formation

or frost penetration at the bottom of the excavation. No pipe or appurtenant structure

shall be installed unless backfilling can be completed before the formation of ice and

frost.

Immediately before joining two lengths of pipe, the inside of the bell and the outside

of the spigot end and the gaskets shall be thoroughly cleaned. Caution shall be exercised

to ensure that the correct type of gasket is used. A thin film of gasket lubricant shall

be applied according to the manufacturer's recommended practices to either the inside

face of the gasket or the spigot end of the pipe or both.

The spigot end of the pipe shall be placed in the socket with care to prevent the joint

from contacting the ground. The joint shall be completed by pushing the pipe home with a

slow steady pressure, without jerky or jolting movements. Stabbing shall not be

permitted. Pipe furnished without a depth mark shall be marked before assembly to ensure

insertion to the full depth of the joint.

Extra care should be used in handling PVC pipe during cold weather due to the reduced

flexibility and impact resistance as temperatures approach and drop below freezing.

Under no circumstances shall a non-disinfected main which cannot be isolated be

connected to an existing, disinfected main. The Responsible Party shall assume and and

all responsibility for damage done by heavily chlorinated water entering existing

facilities due to negligence on his part. All water mains shall adhere to the following

sequence of tests: (1) chlorine; (2) pressure tests; and (3) clearwater test.

204.7	Installation of Valves, Valve Boxes and Manholes

All valves shall be handled in such a manner as to prevent any injury or damage. All

valves shall be thoroughly cleaned before installation. Valves shall be set in such a

manner that the valve stems are plumb. Valves shall be located at points as specified

in subsection 203.8 of these Standards and Specifications. Any deviation from this shall

be at the discretion of the City Engineer.

Final elevation of valve boxes and manholes shall be left to the discretion of the City

Engineer.

Valve boxes shall be installed plumb. Valve boxes which have shifted during backfill

operations and are no longer plumb, shall be re-excavated and realigned to the

satisfaction of the Inspector.

204.8	Testing

Refer to subsection 206 of these Standards and Specifications.

204.9	Backfill

It is expected that the trench excavation shall provide suitable backfill material. Wet,

soft or frozen material, pieces of asphalt or concrete or other undesirable substances

shall not be used for backfill. The backfill material shall be free from rubbish, stones

larger than five inches in diameter, clods and frozen lumps of soil. If the excavated

material is not suitable for backfill as determined by the City Engineer, suitable

material shall be hauled in and utilized and the rejected material hauled away and

disposed of. All snow shall be removed from the trench prior to proceeding with backfill

operations.

Backfilling shall be conducted at all times in a manner to prevent damage to the pipe or

its coating and shall be kept as close to the pipe laying operation as possible.

All backfill around structures shall be consolidated by mechanical tamping.

Backfill in areas where existing pavement is to be cut and replaced, existing material

excavated shall be removed from the site and the trench backfilled with gravel road

base to finished or existing grade as specified in subsection 103.3 of these Standards

and Specifications. Excess material shall be removed prior to surfacing.

204.10	Compaction

Compaction may be obtained by any method approved by the City Engineer, as long as the

backfill material is uniformly compacted throughout the depth of the trench to at least

95 percent of the maximum density obtainable using standard proctor. The minimum moisture

content shall not deviate above or below the standard optimum by more than two percent.

If, in the judgement of the City Engineer, the trench shows signs of being improperly

backfilled or if settlement occurs, the trenches shall be reopened to a depth required

for proper compaction, refilled and recompacted, all in accordance with these

specifications.

Compaction tests, taken by the City Engineer, shall be taken every 200 feet or at the

discretion of the City Engineer while construction is proceeding. The City Engineer shall

pick the location and depths at which all compaction tests shall be taken. All compaction

tests shall be taken at depths below finish subgrade ranging from one foot above the top

of bedding to one foot below grade at an interval not exceeding two feet. The Inspector

shall be present when each test is taken and the results shall be forwarded to the City.

The Responsible Party shall bear the costs of all failed compaction tests.

204.11	Trench Maintenance

During the period of the warranty period, the Responsible Party shall maintain and repair

any trench settlement which may occur and shall make suitable repairs to any pipe,

fitting, valve, valve box, pavement, sidewalks or other structures which may be damaged

as a result of backfill settlement as determined by the City Engineer.

204.12	Repair Fittings

The use of repair clamps, repair sleeves, joint clamps and similar devices is permitted

to repair existing mains not under warranty. Repair clamps shall be of stainless steel

construction in the band, lugs, nuts and stainless steel bolts. These devices should not

be considered substitutions for careful installation of mains. Repair clamp design and

make shall be submitted to the City Engineer for approval prior to installation.

Under no circumstances shall repair clamps be allowed on new installations.

205	WATER SERVICES LINES AND APPURTENANCES CONSTRUCTION SPECIFICATIONS

205.1	General

All water service line construction connecting to the City water system shall be done in

accordance with these Standards and Specifications which shall cover all new water

service line construction from the water main to the property line.

205.2	Materials

All materials furnished shall be new and undamaged. Everything necessary to complete all

installations shall be furnished and installed whether shown on the approved drawings or

not and all installations shall be completed as fully operational.

Acceptance of materials or the waiving of inspection thereof shall in no way relieve the

Responsible Party of the responsibility for furnishing materials meeting the requirements

of these specifications.

The City reserves the right to direct or deny use of certain types of materials in

specific circumstances.

All materials delivered to the job site shall be adequately housed and protected so as to

ensure the preservation of their quality and fitness for the work.

The minimum size allowable for a service line shall be 1-inch diameter.

(a)	Copper Service Pipe - Type "K" or C-901 polyethylene tubing.

Type "K" copper shall be used for service lines 3/4-inch through two-inch diameter.

(b)	Ductile Iron Service Pipe

Ductile iron pipe or PVC C-900 shall be used for service lines larger than two

inches, unless otherwise specified by the City Engineer.

(c)	Corporation and Curb Stops

A curb stop or valve of the same size as the service pipe and conforming to the

following standards shall be installed on every commercial service line larger than

one inch between the water main which is at a point at or near the property line.

Water service saddles shall be cast bronze casting with double silicone bronze

straps, series 183-0 as manufactured by R.H. Baker and Company; Type 323 by Smith-

Blair Inc., or an approved equivalent.

1" corporation stops shall be AWWA taper thread to copper connection of pack joint

and shall be a Mueller No. H-15000 or an approved equal.

Curb stops shall be compression to compression connections and shall be Mueller No.

15154, Oriseal Mark II, with stop, or approved equal.

Curb stop service boxes shall be Mueller H-10302 for 1", H-10304 for 1-1/4" to 2",

Minneapolis pattern, extension type. The curb stop box shall be installed exactly

center over the curb stop valve and in a vertical position. The top lid of the curb

stop box shall be installed a maximum of one inch above the final grade.

205.3	Excavation

Refer to subsection 204.3 of these Standards and Specifications.

205.4	De-Watering

Refer to subsection 204.4 of these Standards and Specifications.

205.5	Pipe Bedding

Refer to subsection 204.5 of these Standards and Specifications.

All specifications are applicable except that "K" copper and C-901 service lines

require a minimum bedding depth of six inches of squeegee for up to a three-inch service

line as shown in the detail drawings. Any service line larger than two inches shall have

typical water main bedding.

205.6	Installation of Pipe

Refer to subsection 204.6 of these Standards and Specifications.

205.7	Installation of Valves and Valve Boxes

Refer to subsection 204.7 of these Standards and Specifications.

205.8	Testing

Refer to subsection 204.8 of these Standards and Specifications.

205.9	Backfill

Refer to subsection 204.9 of these Standards and Specifications.

205.10	Compaction

Refer to subsection 204.10 of these Standards and Specifications.

205.11	Location

That portion of the service pipe between the main and curb stop, must be in a continuous

straight line, with no joints and perpendicular, if possible, to the line of the main.

The main to be tapped must extend along the entire length of the lot line of the property

to be served.

If service is requested for a lot at the end of a cul-de-sac street, the main to be

tapped must be not more than 25 feet from the curb line or the proposed curb line at

the end of the cul-de-sac. The service pipe between the main and the property line in

cul-de-sacs shall be in a continuous straight line and shall enter the property a

distance of two to four feet from the nearest lot corner. No service line may be

constructed through or in front of adjoining property. When possible, the service line

shall be located five feet toward the high side of the lot from the center line of the

lot. Service lines are not to extend beneath driveways unless otherwise approved by the

City Engineer. Sewer and water service lines must be a minimum of 10 feet apart

horizontally or special protection and/or special installation design of the services

shall be required. Water service locations shall also be marked with a "V" on the curb.

Markings shall be neatly stamped, chiselled or sawcut, not painted.

205.12	Depth

All service pipe must be laid at least 4-1/2 feet below the established grade of the

street in which they shall be laid and all other places at least 4-1/2 feet below the

surface of the ground. If in the judgement of the City Engineer, the topography indicates

the advisability thereof, service pipe shall be laid to a lower depth as required by the

City Engineer on the basis of then existing information.

If after a service pipe has been installed, the grade of the surface of the ground is

lowered, the service pipe must be lowered to provide at least 4-1/2 feet of cover.

205.13	Separate Trenches

Except as hereinafter provided, service pipe may not be installed in a trench containing

other conduits which convey any substance other than potable water. The trench containing

the service pipe shall be separated laterally from trenches containing other conduits by

at least 10 feet of undisturbed compacted earth. In certain residential installations,

the City Engineer may approve variations to the separate trench requirement.

205.14	Connections

Service pipe two inches or less in diameter shall be connected to the main by means of a

bronze corporation stop of the same size.

No underground joints are allowed in the copper or polyethylene service pipe between the

corporation stop and the curb stop. The use of underground joints may be allowed only on

the repair of existing service lines with specific approval from the City Engineer.

Meters shall be of the same size as that portion of the service pipe between the meter

and the main unless otherwise stated by the City Engineer. Oversizing of service lines

between the meter and the building is permitted, outside of the pit or vault.

Taps shall not be made on a water main until the main has passed the chlorine and

hydrostatic pressure tests and clearwater tests.

Care shall be taken to properly install water service lines so that enough slack is in

the service lines to protect against pullout problems.

Water mains shall be tapped at a 45 degree angle from the horizontal centerline of the

water main on the same side of the pipe as the water meter.

Service taps shall have a minimum separation of 24 inches and be no closer than 24 inches

to a coupling or pipe joint or fitting. No more than four service taps shall be permitted

on any one joint of pipe.

205.15	Pumps

Except when specifically authorized by the City Engineer, the installation of pumps on

service pipes designed to increase water pressure inside the premises receiving service

is prohibited.

205.16	Lawn Sprinklers

Lawn sprinkler systems must be tapped on the outlet side of the meter or a direct tap on

the main line with a meter setting.

Approved vacuum breakers or other means of cross connection control as required by the

Scottsbluff Municipal Code are required with each sprinkler system. All devices utilized

for cross connection must meet the minimum requirements of AWWA, the Uniform Plumbing

Code, as well as the approval of the City Engineer. A list of approved cross connection

control devices can be obtained at the City.

205.17	Abandonment

Only one domestic tap is allocated per single family residence. If it is necessary to

abandon an existing water tap, it shall be turned off and disconnected at the main,

unless otherwise specified by the City Engineer. A charge shall be assessed for all

labor and materials necessary to perform this work. Service lines that have been

installed in improper locations, such as side yards or corner lots, shall be moved to

the location noted in these Standards and Specifications as long as such action does

not require the cutting and patching of existing surfacing. A compression fitting shall

be utilized if necessary to relocate a meter pit from a driveway area, only if the

installation of a new service line would require the cutting and patching of existing

surfacing.

206	WATER MAIN RELEASE PROCEDURE

206.1	Scope

This procedure is to be followed when releasing a newly installed water main or

releasing a repaired pre-existing water main. It covers disinfection, bacteriological

sampling and reporting of results.

206.2	New Main

Installation shall be in accordance with established AWWA standards (AWWA C-600 or C-603)

with particular attention paid to the provision for cleanliness within the pipe itself.

Flushing and disinfection shall be performed by the Responsible Party in accordance with

AWWA Standard C-601 (more detailed instructions shall be found below.) Sampling

(bacteriological and chlorine residual) shall be performed by the Responsible Party in

the presence of the Inspector. Chlorine residual analysis shall be performed using

accepted test procedures in Standard Methods for the Examination of Water and Wastewater.

Bacteriological testing shall be performed by a laboratory certified by the Nebraska

Department of Health. The cost of all testing shall be the responsibility of the

Responsible Party.

206.3	Repaired Mains

After a main has been repaired and flushed, personnel from the Scottsbluff Water

Department shall inspect the water for color, turbidity and chlorine residual, prior

to restoring the repaired main into service.

206.4	Disinfection

Disinfection shall be accomplished in accordance with the Nebraska Department of Health.

206.5	Flushing

After chlorination or disinfection of the pipeline, flushing shall commence to remove the

chlorine solution. Flushing shall continue for a minimum of five minutes beyond the time

when chlorine residual is 0.3 ppm or less.

206.6	Hydrostatic Testing

No hydrostatic tests shall be made on any portion of the pipeline until all field placed

concrete has had adequate curing time as defined for thrust blocks in subsection 204.1(l)

of these Standards and Specifications and all compaction test results have been

submitted to and approved by the Inspector. Only potable water may be used in testing

procedures. See Table 200-2.

The pipeline shall be tested in accordance with AWWA C-600 or C-603 except as follows:

The pipeline shall be tested with water at a pressure of 150 psi or 50 psi above

working pressure, whichever is greater.

The City Engineer shall be notified 24 hours in advance of testing. All acceptance

testing shall be made in the presence of the City Engineer only after the pipeline is

in a state of readiness for testing.

All air in the line shall be properly purged. Where blowoffs or hydrants are not

available or effective in purging air from the line, the City Engineer shall require a

tap to purge the line. The location and size of the tap shall at the City Engineer's

discretion. The cost for such a tap shall be borne by the Responsible Party.

No leakage is allowed through the bonnet of the line valve. Any valve leaking through

the bonnet shall be removed and replaced.

The pressure test shall be a two hour test taken at the high point in the line. Every

time the water line pressure drops five psi, the pump shall be started to bring the line

pressure back to the initial pressure. At the Inspector's discretion, a minimum of a one

hour pressure test may be conducted in lieu of a two hour test.

Polyvinyl chloride or ductile iron pipe shall be considered to have passed the pressure

test when the total leakage in 24 hours is less than 11.5 gallons per inch of inside

diameter per mile of pipeline. The City Engineer shall direct the Responsible Party to

repair specific leaks regardless of test results, if in his opinion they are serious

enough to endanger the future service of the pipeline. Pipelines shall be tested in

sections as rapidly as such section may be isolated. Should any leakage of the pipeline

become apparent during the warranty period, the Responsible Party shall perform the

necessary repairs. If the Responsible Party does not initiate the repair within 4 hours

of notice the City shall perform the necessary repair and the Responsible Party shall be

invoiced for all work performed. Blowoffs, pressurizing pump, corporation stops, and

water measuring apparatus shall be provided by the Responsible Party, or at his expense.

At the Inspector's discretion, measuring apparatus may be required to be calibrated by

the City Engineer at the Responsible Party's expense.

The City shall not be held responsible for water tightness of its valves on existing

facilities. If existing valves leak, the City shall assist in reducing the influx of

water, but the Responsible Party must use methods at his own disposal to work with the

resulting leakage.

All fire hydrant lines shall be pressure tested. It is recommended that the fire hydrant

be dry. All fire hydrants shall be tested by flushing each hydrant a minimum of five

minutes before they shall be accepted.

All fire lines shall be pressure tested at 200 psi.

206.7	Bacteriological Sampling

Sampling shall be completed in accordance with the Nebraska Department of Health. The

Responsible Party shall take the required samples, in the presence of City personnel,

and submit the samples to a laboratory approved by the Nebraska Department of Health.

207	WATER METER INSTALLATION STANDARD SPECIFICATIONS

207.1	General Information

(a)	Inside Installations

Water meter installations inside any building are recommended if at all possible.

(b)	Jumper Pipes

Jumper pipes are not permitted.

(c)	Water Meters

All water meters, regardless of size, connected to the City's utility system, shall

be purchased from and remain the property of the City. Under no circumstances shall

anyone other than City personnel remove a water meter once the installation has been

inspected and approved, unless otherwise specified by the City Engineer.

(d)	Meter Sizes

All meter sizes for residential, commercial or industrial use shall be determined

by the consulting engineer and calculations submitted to the City Engineer for

review and approval. Calculations shall be based on design criteria with AWWA manual

M22 "Sizing Water Services Lines and Meters."

(e)	All commercial meters, regardless of size, and any other meter installation which

poses a possibility of creating a health hazard, must receive an inspection by the

City Water Department personnel prior to a meter release.

208	CROSS CONNECTIONS

208.1	Definition

For use in this section, a cross connection shall be defined as "any physical

arrangement whereby a public water supply is connected, directly or indirectly with any

nonpotable or unapproved water supply system, sewer drain, conduit, pool storage

reservoir, plumbing fixture, or other device which contains or may contain any

contaminated water, liquid, or other waste of unknown or unsafe quality that could

impart a contaminant to the public water supply as a result of backflow."

208.2	Types of Cross Connection Control Devices

(a)	Approved Air Gap Separation

An approved air gap is a physical separation between the free-flowing discharge end

of a potable water supply pipeline and the top of an open or non-pressure receiving

vessel.

Installation

1.	An approved air gap is not always practical and is vulnerable to bypass

arrangements which nullify its effectiveness; however, in extremely hazardous

installations, an approved air gap separation is recommended.

2.	The vertical, physical separation between pipeline and vessel must be at least

twice the diameter of the inlet pipe and never less than one inch.

3.	The inspection of air gaps should be included in the yearly testing program

for backflow devices.

(b)	Reduced Pressure Principal Backflow Prevention Device (RPBD)

The reduced pressure principal backflow device consists of two independently

acting, internally loaded approved check valves separated by a reduce pressure

zone. This device shall be installed horizontally as a unit between two tightly

closing shutoff valves. During normal operation, the pressure between the two check

valves is maintained at a lower pressure than the supply pressure. If either check

valve should leak, the differential pressure relief valve shall maintain a

difference of not less than two psi between the supply pressure and the zone between

the two check valves by discharging to the atmosphere.

The RPBD is normally used in locations where an approved air gap or a barometric

loop is impractical. This device is effective against backflow caused by

backpressure and backsiphonage and is used to protect the water system from

substances which are hazardous to health.

Ball valves shall be accepted in lieu of gate valves on any backflow preventor.

Installation

1.	The RPBD shall be installed with adequate space to facilitate maintenance

and testing. An RPBD shall be inspected and tested as soon as possible after

installation to insure its satisfactory operation and proper installation.

2.	It is important that some models of RPBDs be installed 12 inches, plus nominal

size of the device, above the ground or bottom of vault because the removal of

the pressure relief valve requires a minimum of 12-inch clearance. Also, some

devices require a minimum wall clearance for driving the pins from the check

valves.

3.	An RPBD installation shall not be approved for any pit or vault location

below ground level. Semi-buried pits are acceptable if the RPBD is installed

above the ground level with an approved air gap between the relief valve port

and daylight drain. The daylight drain from above ground or semi-buried

vaults must:

a.  Be able to be bore sighted;

b.  Installed above the ground level;

c.  Be able to handle the volume of water that can be discharged from the

relief valve port.

4.	The RPBD shall be installed horizontally with four test cocks properly placed

for testing purposes.

5.	No bypasses shall be allowed around any backflow preventor unless the same

approved backflow prevention device is installed on the bypass.

6.	The device shall be protected from freezing. Various heating elements are

effective if power is available. If the system can be drained, additional

"frost-proofing" can be accomplished by drilling and tapping holes, at

carefully selected points as instructed by the manufacturer, in the

compartments which trap water.

7.	Care should be taken to insure the device is not installed where the pressure

can be maintained above the devices rated capacity.

8.	If hot water conditions are anticipated, inquire as to the manufacturer's

recommendations.

9.	When the RPBD is located inside a building, a drain pipe or other approved

adequate drainage shall be provided for the relief valve port.

10.	If a drain is to be provided for the relief valve port, there shall be an

approved air gap between the port and the drain.

11.	Size the device hydraulically to avoid excessive pressure loss. The head loss

is not necessarily directly proportional to flow. Some devices have a high

loss at low flows and a low loss at high flows.

12.	A strainer shall be required ahead of the device when determined by the City

Engineer.

13.	Thoroughly flush the lines prior to installing an RPBD.

(c)	Double Check Valve Assemblies (DCVA)

This device consists of two internally-loaded approved check valves, either spring

loaded or internally weighted, installed horizontally as a unit between two tightly

closing shutoff valves. This device is effective against backflow caused by

backpressure and backsiphonage and is used to protect the water system from

substances which are not hazardous to health.

Ball valves shall be accepted in lieu of gate valves on any backflow preventor.

Installation

1.	A DCVA shall be installed with adequate space to facilitate maintenance and

testing. A DCVA shall be tested and inspected as soon as possible after

installation to insure its satisfactory operation and proper installation.

2.	The device shall be protected from freezing.

3.	If hot water conditions are anticipated, inquire as to the manufacturer's

recommendations.

4.	A DCVA installation shall not be approved for any pit or vault location below

ground level. Semi-buried pits are acceptable if the DCVA is installed above

ground with an approved air gap between the bottom of the device and the day-

light drain. The daylight drain from above ground or semi-buried vaults must:

a.  Be able to be bore sighted,;

b.  Be installed above the ground level.

5.	The DCVA shall be installed horizontally with four test cocks properly placed

for testing purposes.

6.	No bypasses shall be allowed around any backflow preventor unless the same

approved backflow prevention device is installed on the bypass.

7.	When the DCVA is located inside a building, adequate floor drainage shall be

provided to allow for device testing.

8.	A strainer shall be required ahead of the device when determined by the City

Engineer.

9.	Thoroughly flush the lines prior to installing a DCVA.

(d)	Vacuum Breakers (VB)

Vacuum breakers, either pressure or atmospheric, are effective against backsiphonage

only and can not be used in an area where a positive pressure can be developed on

the downstream side of the device or in an area where the vacuum breakers are

subject to flooding. Vacuum breakers are not acceptable backflow protection at

premises service connections other than lawn sprinkler systems. When vacuum breakers

are installed in a line which shall reach a temperature of 160 degrees F. or above,

a hot water type vacuum breaker shall be used.

1.	Pressure Vacuum Breaker with Internal Check Valve (PVB)

Pressure vacuum breaker assemblies consist of a check valve (sometimes two),

vacuum relief, inlet and discharge shutoffs and properly installed test cocks.

The pressure vacuum breaker has a vacuum relief valve which is internally

loaded, normally by means of a spring. This spring loading allows the device

to be installed on the pressure side of a shutoff valve.

Installation

This device shall be installed a minimum of 12 inches above the highest outlet

and/or overflow level on the nonpotable system. Vacuum breakers shall not be

installed more than five feet above the ground. Adequate room shall be made

available for maintenance and testing.

2.	Atmospheric Vacuum Breaker (AVB)

An atmospheric vacuum breaker is a device which allows air to enter the water

line when the line pressure is reduced to a gauge pressure of zero or below.

The atmospheric vacuum breaker is designed to prevent backsiphonage only. It

is not effective against backflow due to backpressure and shall not be

installed where it shall be under continuous pressure for more than 12 hours

in any 24-hour period.

Poppets of all atmospheric vacuum beakers shall be precision fitted to insure

positive closure.

Installation

This device shall be installed downstream of the last shutoff valve and a

minimum of six inches above the highest outlet and/or overflow level on the

nonpotable system. Vacuum breakers shall not be installed more than five

feet above the ground. It is not recommended for use in areas where water is

discharged on a sustained basis because the poppet valve shall tend to stick

and not work properly.

208.3	Mandatory Backflow Prevention Installations

List of suspected high-hazard installations:  The following general fields of

installations shall be required to have backflow prevention devices installed on all

high hazards.

1.	Funeral Homes

2.	Hospitals (Clinics, including Veterinary Clinics, Etc.)

3.	Plating and Chemical Companies

4.	Labs (Industrial and Medical)

5.	Packing Houses and Rendering Plants

6.	Manufacturing Plants

7.	Lawn and Irrigation Systems

8.	Car Washes

9.	Nursing and Convalescent Homes

10.	Professional Building (Doctors, Dentists, Etc.)

11.	Retail Complexes

12.	Schools

13.	Motels and Hotels

14.	Laundry and Cleaners

15.	Major Office Buildings

16.	Apartment Houses (High rise over 40 feet high)

In applying the recommendations outlined in this Section, it is vital that the degree of

protection provided must be commensurate with the degree of hazard present. In situations

where health hazards, or unknown hazards exist, the air gap separation, when properly

maintained, or the reduced pressure principle backflow device should be used because

they offer the highest known degree of reliability.

The double check valve assemblies or vacuum breakers may be utilized where aesthetic

problems or undesirable situations may occur. Approval by the City Engineer must be

given in these instances.

208.4	Approved Backflow Prevention Devices

The City has a list of approved backflow devices.

SECTION 300

SANITARY SEWER SYSTEM STANDARDS

SECTION 300 - SANITARY SEWER SYSTEM STANDARDS

TABLES OF CONTENTS

PAGE

301	GENERAL PROVISIONS		300-1

302	SANITARY SEWERS - DESIGN CRITERIA	                     300-1

302.1	Scope		                     300-1

302.2	General			300-1

302.3	Design Criteria		300-1

302.4	Flow Calculations		300-2

302.5	Lift Stations		300-3

302.6	Oversizing of Mains		300-3

302.7	Materials			300-3

302.8	Ground Cover		300-3

302.9	Locations			300-4

302.10	Crossings			300-4

302.11	Manholes			300-5

302.12	Underdrains		300-5

202.13	Grease and Sand/Oil Interceptors		300-5

303	SANITARY SEWERS CONSTRUCTION SPECIFICATIONS	300-6

303.1	Materials			300-6

303.2	Excavation		300-8

303.3	Dewatering		300-9

303.4	Pipe Bedding		300-9

303.5	Installation of Pipe		300-9

303.6	Manhole Construction		300-10

303.7	Backfill			300-11

303.8	Compaction		300-11

303.9	Trench Maintenance		300-11

303.10	Testing			300-11

304	SANITARY SEWER SERVICE LINES AND APPURTENANCES

CONSTRUCTION SPECIFICATIONS		300-14

304.1	General			300-14

304.2	Materials			300-14

304.3	Excavation		300-15

304.4	Dewatering		300-15

304.5	Pipe Bedding		300-15

304.6	Installation of Pipe		300-15

304.7	Manhole Construction		300-15

304.8	Backfill			300-15

304.9	Compaction		300-15

304.10	Location and Alignment of Service		300-15

304.11	Service Stub-Ins to Property Line		300-16

304.12	Connections		300-16

304.13	Commercial and/or Industrial Manholes	300-17

304.14	Infiltration		300-17

DETAIL DRAWINGS

300-2	Sewer Main Bedding, Underdrain and Service Connection Detail

300-3	Standard Manhole Detail

300-4	Drop Manhole Detail

300-5	Semi-Drop Manhole Detail

300-6	Plastic Manhole Step

300-7	Standard Clean-Out Detail

300-8	Sand and Oil Interceptor Type "A" Detail

300-9	Grease Interceptor Type "A" Detail

300-10	Grease Interceptor Type "B" Industrial

300-11	Sand and Oil Interceptor Type "B" Industrial

300-12	Oil and Grease Interceptor Industrial

SECTION 300 - SANITARY SEWER SYSTEM STANDARDS

301	GENERAL PROVISIONS

These standards are promulgated by the City Engineer of the City of Scottsbluff.

Interpretation, enforcement and revision of these standards has been delegated to the

City Engineer.

302	SANITARY SEWERS DESIGN CRITERIA

302.1	Scope

The purpose of this section of the Standards and Specifications is to set forth the

general criteria to be used in the design of sanitary sewers and appurtenances in the

City of Scottsbluff and outlying areas. Any deviation from these standards shall be

approved and supported by the City Engineer in writing.

302.2	General

All sanitary sewer mains and appurtenances shall be in conformance with these Standards

and Specifications and shall be designed by or under the direct supervision of a

registered professional engineer licensed to practice in the State of Nebraska.

302.3	Design Criteria

Sanitary sewers must be designed to carry the peak discharge with the pipe being no more

than 50 percent full for collection mains or 80 percent full for outfall mains, and be

able to transport suspended material such that deposits in the sewer are precluded. It is

essential that the sewer have capacity for peak hourly sewage flow and adequate velocity

at minimum sewage flows.

All sewers shall be designed and constructed to give velocities of not less than two feet

per second nor more than 10 feet per second based on the Manning approximation of the

Kutter Formula using an "n" value of 0.013. Use of other practical "n" values may be

permitted, if justified, on the basis of research and field data and approved by the

City Engineer.

MANNING FORMULA

V      = mean velocity

V = 1.486 R2/3 S1/2               R      = hydraulic radius

n                          S      = slope of energy grade

n      = coefficient of roughness

The minimum and maximum slopes generally permissible for sewer collection and outfall

mains are provided by NDEQ.

The Uniform Plumbing Code shows the minimum and maximum allowable slopes for sanitary

sewer service lines.

302.4	Flow Calculations

Wastewater flow calculations are required for all proposed developments, unless otherwise

waived by the City Engineer. All flow calculations shall be submitted to the City

Engineer for review along with the engineering plans.

Calculations shall include:

1.	The average and peak quantity of sewage flow projected to be generated by the

project.

2.	The velocity of flow in the pipe.

3.	The percent of pipe full.

4.	The impact on downstream sewer systems.

5.	The nature of any wastes not ordinary domestic sewage.

6.	The quantity and type of discharge of an unusual nature such as swimming pool

drainage, cooling water, etc.

For commercial buildings (if required): Volume, BOD, SS, nature and type of activity

expected.

The following design criteria shall be used for projecting wastewater flows, unless more

site specific criteria are available.

Residential

100 gallons per person per day (gpd)

low density (less than 5 DU/Ac.)   = 3.45 people/unit

mid density (5 to 12 DU/Ac.)       = 2.45 people/unit

high density (more than 12 DU/Ac.) = 2.20 people/unit

Commercial

1000 gallons per acre per day

Industrial

1000 gallons per acre per day

Peaking Factor

Peak flows shall be calculated utilizing the following equation:

PF =  1.72        [3.5 max., 2.0 min.)

(F)0.295

where PF = Peaking Factor

F = Average Flow in MGD

302.5	Lift Stations

Where lift stations are proposed, a basin study shall be completed by the consulting

engineer. The basin may include properties other than the proposed development, and costs

for sizing of facilities within the basin shall be allocated as documented pursuant to

the City code of ordinances.

Lift stations shall be sized for peak wastewater flows. Force mains shall be sized for

peak wastewater flows. Force mains shall be sized for a maximum velocity of six fps,

minimum velocity of two fps.

Lift stations shall be of Smith-Loveless Package System Design, or equivalent, with a

clean water supply. Other designs of lift stations may be submitted, depending on the

application.

All controls and electrical components shall be housed in a weatherproof enclosure

above ground and adjacent to the wet well.

Emergency power shall be provided for the lift stations, sized to run the entire lift

station at capacity. A LP/Natural Gas diesel generator shall be provided in a walk-in

above ground enclosure on a concrete pad. The fuel tank shall be sized to permit 24

hours of run time. Automatic telephone call systems shall be installed in each lift

station.

Shop drawings for the lift station and related equipment shall be submitted to the City

Engineer, a minimum of two weeks prior to construction, for approval.

302.6	Oversizing of Mains

No sanitary sewer main shall be less than eight inches in diameter. Oversizing of mains

may be required by the City, as required by other applicable ordinances of the City of

Scottsbluff.

302.7	Materials

Only sanitary sewer mains constructed of the following materials are permitted:

Polyvinyl Chloride Pipe (PVC) ASTM 3034, SDR 35

Polyvinyl Chloride Pressure Pipe C-900, DR-18/DR-24

All materials shall conform with the material requirements as set forth in subsection

303.2 of these Standards and Specifications.

302.8	Ground Cover

All sewer mains and service lines shall be designed so that a minimum of four feet of

cover exists over the pipe after final grade has been established, unless specifically

approved by the City Engineer.

Sewer mains and service lines which have less than four feet of cover or more than 15

feet of cover shall be installed using polyvinyl chloride pressure pipe, as specified

in subsection 204.1(b). Under no circumstances shall a sewer have less than three

feet of coverage, unless specifically approved by the City Engineer in writing. Sewer

lines which must cross under irrigation ditches or through bogs or swamps where the

soil is unstable and water infiltration may be high, must be specifically designed by

the consulting engineer and approved by the City Engineer.

302.9	Location

All mains shall be installed in dedicated streets, alleyways or easements. Location for

sewer mains located in street right-of-ways shall be six feet from the back of curb on

the south or east side of the street. Sewer mains shall installed on the centerline of

alleyways. In addition, a minimum separation of five feet from the lip of pan or edge of

pavement is required for the sanitary sewer main, unless otherwise specified by the City

Engineer.

Sewer mains shall be installed in exclusive easements, either by plat or separate

document, when, as determined by the City Engineer, it is not practical to make such

installation in a dedicated alley. Under no circumstances shall any structures be

constructed within these easements or rights-of-way without prior approval, including

terms and conditions, as set forth by the City. The minimum width requirements for

sanitary sewer easements are 20 feet or twice the depth of the pipe, whichever is

greater. The pipeline shall be centered in the easement, and offset a minimum of five

feet from any property line. In the event two utility lines share the same easement, the

minimum width for the easement shall be 30 feet.

All sanitary sewer lines and manholes must be located so that they are accessible to

the City of Scottsbluff maintenance crews at all times.

No curvilinear sewers shall be permitted.

Sanitary sewers shall not be installed in drainage ditches or detention/retention ponds.

The minimum vertical separation between pipes shall be 18 inches, and the minimum

horizontal separation between pipes shall be ten feet. All distances shall be measured

edge to edge.

302.10	Crossings

Complete installation in accordance to NDH and NDEQ guidelines.

Under no circumstances shall the vertical clearance between any lines involving a water

or sanitary sewer line be less than 18 inches without specific written authorization

from the City Engineer. Special design requirements, such as concrete cradles, may be

required by the City Engineer for certain crossing situations.

302.11	Manholes

Manholes shall be installed at both end of each line, at changes in grade, size, or

alignment at intersections and at distances not greater than 400 feet for sewers 15

inches in diameter or less, 450 feet for sewers 18 inches and 21 inches in diameter, and

500 feet for sewers 24 inches in diameter and larger.

A drop manhole shall be provided for a sewer entering a manhole at an invert elevation of

24 inches or more above the manhole invert. Where the difference in elevation between the

incoming sewer invert and the manhole invert is less than 24 inches, the invert shall be

shaped in a filleted fashion to prevent solids deposition, as shown in the detailed

drawings under semi-drop manhole. Drops should be avoided whenever possible.

The internal diameter of the manhole barrel shall not be less than 48 inches for sanitary

sewers of sizes 18 inches or less, 60 inches for sizes 21 inches to 27 inclusive, and 72

inches for sizes 36 inches and larger.

The flow channel through the manhole shall be made to conform to shape and slope to that

of the sewers. A minimum two-tenths fall across manholes shall be maintained.

Under no circumstances shall a manhole be located in concrete areas, such as sidewalks,

cross pans, aprons, curbs and gutters.

302.12	Underdrains

Underdrains shall only be allowed after obtaining the approval of the City Engineer.

Underdrains on sanitary sewer service lines shall be similar in nature as those shown in

the detailed drawings. Such drains shall not discharge into sanitary sewer manholes, and

underdrains shall not be vertically aligned above a sanitary sewer, unless specifically

authorized by the City Engineer.

302.13	Grease and Sand/Oil Interceptors

All commercial operations involved in food preparation, automotive servicing, or any

other business or industry discharging any grease, sand, or oil into the City sanitary

sewer system shall be required to install a grease or sand/oil interceptor.

(a)	Grease Interceptors

All interceptors shall be located outside, within 30 feet of the facility served

and shall be easily accessible at all times for inspection and maintenance. All

interceptors shall be concrete and of a single, precast monolithic pour and shall

be installed in accordance with the detail drawings. Smaller, in-line grease

interceptors shall be permitted only where larger interceptors are impractical and

upon the specific approval of the City Engineer.

Sizing calculations are to be prepared by the consulting engineer and submitted to

the Wastewater Treatment Plant Superintendent per the Uniform Plumbing Code.

(b)	Sand/Oil Interceptors

1.	Location/Design

The sand/oil interceptor shall be designed in accordance with the Uniform

Plumbing Code with the addition of the following:

a.  All sand and oil interceptors shall be located outside, within 30 feet and

not less than five feet of the facility, unless specifically authorized by

the City Engineer. Interceptors shall be accessible for inspection and

maintenance.

b.  All sand and oil interceptors shall have two compartments, the smallest of

which shall have at least one-third the capacity of the entire interceptor.

2.	Sizing

a.  Sizing calculations are to be prepared and submitted to the City Engineer

per the following method:

1.  Three-inch diameter floor drains shall be rated at six fixture units.

2.  Four-inch diameter floor drains shall be rated at eight fixture units.

3.  One fixture unit equals 7.5 gpm.

4.  The sizing formula shall be as follows: Fixture units connected x

7.5 gpm x 5 minutes - interceptor size.

b.  Where trough drains are used, each bay or compartment area equalling the

square foot surface of a standard service station bay which is served by

the trough drain shall be rated at six fixture units per bay. Vehicle

wash drains shall be rated at eight fixture units each, regardless of size.

c.  No combination sand and oil interceptor smaller than 320 gallons capacity

shall be installed at a single bay facility.

d.  All interceptors shall be installed in accordance with the detail drawings.

e.  Cleanouts are required immediately downstream of the sand and oil

interceptor.

303	SANITARY SEWERS - CONSTRUCTION SPECIFICATIONS

303.1	Materials

All materials furnished shall be new and undamaged. Everything necessary to complete all

installations shall be furnished and installed whether shown on approved drawings or not

and all installations shall be completed as fully operational.

Acceptance of materials or the waiving of inspection thereof shall in no way relieve the

Responsible Party of the responsibility of furnishing materials meeting the requirements

of the specifications.

The City Engineer reserves the right to direct or deny use of certain types of materials

in specific circumstances.

All materials delivered to the job site shall be adequately housed and protected so as to

ensure the preservation of their quality and fitness for the work.

(a)	Polyvinyl Chloride Pipe

All pipe materials and fittings shall meet the extra strength minimum requirements

of ASTM D-3034, SDR-35, or latest revision thereof.

Pipe shall be subjected to drop impact tests in accordance with ASTM D-2444.

All fittings and accessories shall be as manufactured and furnished by the pipe

supplier or approved equal and have bell and/or spigot configurations compatible

with that of the pipe.

Pipe stiffness for all pipe sizes shall be tested in accordance with ASTM D-2412,

while joint tightness shall be tested in accordance with ASTM D-3212.

Installation shall be in accordance with Ring-Tite PVC Gravity Sewer Pipe

Installation Guide TR-614A published by John-Mansville, except as modified by these

Standards and Specifications.

If deflection limits exceed five percent the Responsible Party shall be responsible

for removing the existing pipe and installing a new pipe material under the

direction of the City Engineer.

The manufacturer shall furnish a certified statement that the inspection and all of

the specified tests have been made and the results thereof comply with the

requirements of the applicable standard(s) herein specified. A copy of the

certification shall be sent to the City Engineer upon request.

(b)	Polyvinyl Chloride Pressure Pipe

Refer to subsection 204.1(b) of these Standards and Specifications.

(c)	Manholes

Manholes shall be constructed of precast concrete. Ring and cover shall be cast-

iron, 24-inch cover diameter, with a combined weight of not less than 400 pounds,

similar and equal to the "Denver Heavy" pattern. Manhole steps shall be aluminum,

Alcoa No. 20100, as manufactured by the Aluminum Company of America, or approved

equivalent, or plastic coated steel steps manufactured by N.A. Industries, Inc. #PS-

2-PF-S, or approved equivalent, spaced 12 inches on center, aligned away from the

invert over largest bench. All cones shall be eccentric.

Precast manhole risers and cones shall be manufactured in accordance with ASTM

Designation C-478.

Manhole rings shall be 30-inch diameter, with 24-inch insert and cover, for 60-

inch and 72-inch diameter manhole barrels.

The performing flexible plastic joint sealing compound shall be "RAMNEK" as

manufactured by K.T. Snyder Company, or approved equal. The application of the

priming compound and the sealing compound shall be accomplished in strict

conformance with the manufacturer's instructions as to the quantity of material,

the grade of the materials and the application temperature. This plastic joint

compound shall be applied to all manhole joints.

The cone section shall not extend closer than 12 inches to the top of the manhole

cover. Precast concrete adjustment rings shall be used on top of the cone to

support and adjust the manhole frame to the required final grade. Use of bricks

to adjust the frame is not permitted.

The manhole barrels shall be watertight at all joints and riser sections.

Flat top sections may be used on shallow lines where cone sections are impractical

to use as specified by the Engineer.

Concrete bases shall be poured in place, Class "47B" concrete, with a minimum

thickness of 18 inches. Manhole inverts shall be formed as indicated in the detail

drawings to ensure smooth flow through the manhole. Precast bases may be used in

lieu of poured in place bases.

Refer to the sewer manhole detail drawing.

(d)	Drop Manholes

A drop manhole shall be constructed at all manholes where the incoming pipe invert

is more than two feet above the manhole invert.

Refer to detail drawing for drop manholes. Drop manholes shall be constructed in

accordance with this detail.

(e)	Semi-Drop Manholes

A semi-drop manhole shall be constructed at all manholes where the incoming pipe

invert is up to two feet above the manhole invert pipe outlet. Refer to detail

drawings of semi-drop manholes.

(f)	Concrete

Refer to subsection 204.1(m) of these Standards and Specifications.

303.2	Excavation

Refer to subsection 204.3 of these Standards and Specifications.

303.3	Dewatering

All pipe trenches or structure excavation shall be kept free from all water during pipe

laying and other related work. The method of dewatering shall provide for a completely

dry foundation at the final lines and grades of the excavation. All water shall be

disposed of in a suitable manner without being a menace to public health or causing a

public inconvenience. The dewatering operation shall continue until such time as it is

safe to allow the water table to rise in the excavation. Pipe trenches shall contain

enough backfill to prevent pipe flotation.

303.4	Pipe Bedding

After completion of the trench excavation and proper preparation of the foundation, bell

holes shall be dug deep enough to provide a minimum of two inches of clearance between

the bell and the bedding material or according to the pipe manufacturer's recommended

bedding practices. All pipe shall be installed in such a manner as to ensure full support

of the pipe barrel over its entire length. After the pipe is adjusted for line and grade

and the joint is made, the bedding material shall be carefully placed and tamped under

the haunches of the pipe up to spring line and in the previously dug bell holes. The

bedding shall then be installed to a minimum of six inches and a maximum of 12 inches

above the top of the pipe, no matter what type of pipe is being installed. The bedding

material shall conform to the manufacturer requirements.

303.5	Installation of Pipe

Pipe and fittings shall be loaded and unloaded by lifting so as to avoid shock or

damage. Under no circumstances shall such material be dropped. Before the placing of

pipe in the trench, each pipe or fitting shall be thoroughly cleaned of all foreign

material, kept clean at all times and examined for cracks or defects before

installations. The Inspector may reject any pipe which shows discoloration due to the

sun.

Joint lubricant shall be as supplied by the pipe manufacturer.

Pipe shall be laid upstream with spigot ends pointing downstream. All pipe is to be

placed true to line and grade with ends abutting, carefully centered and with a smooth

invert at the joint. The joint shall be made in a workmanlike manner so as to be

watertight. New installations shall be complete and flushed prior to connecting to

existing lines.

Whenever the pipe is left unattended, including prior to any connection, temporary plugs

shall be installed at all openings. Temporary plugs shall be watertight, standard cast

iron and of such design as to prevent children and animals from entering the pipe. All

temporary plugs shall be approved by the Inspector.

No pipe or appurtenant structure shall be installed upon a foundation into which frost

has penetrated or at any time when the Inspector deems there is a danger of ice

formation or frost penetration at the bottom of the excavation. No pipe or appurtenant

structure shall be installed unless backfilling can be completed before the formation of

ice and frost.

Immediately before joining two lengths of pipe, the inside of the bell, the outside of

the spigot end, and the gasket shall be thoroughly cleaned. Caution shall be exercised

to ensure the correct type of gasket is used. A thin film of gasket lubricant shall be

applied to either the inside face of the gasket or the spigot end of the pipe or both,

according to the pipe manufacturer's installation procedure.

The spigot end of the pipe shall be placed in the socket with care to prevent the joint

from contacting the ground. The joint shall be completed by pushing the pipe home with

a slow, steady pressure. Stabbing shall not be permitted.

Repair couplings shall not be permitted unless specifically authorized by the City

Engineer.

All sewer lines installed at minimum grade shall have final grade field verified by

the City Engineer, prior to backfill. This shall also be performed after the backfill and

compaction of trench area is complete in place above the pipe.

Under no circumstances shall sewer lines be installed beneath any concrete, such as

sidewalks, curbs or gutters unless authorized by the City Engineer.

Sewers shall be located a minimum of ten feet horizontally from existing or proposed

water lines (edge of pipe distance). Where sewer lines cross water mains or storm sewers,

the sewer pipe shall be a minimum of 18 inches clear distance vertically from the other

main. If this clear distance is not feasible, the crossing must be designed and

constructed so as to protect the higher main. Minimum protection shall consist of the

installation of an impervious and structural sewer (i.e., polyvinyl chloride pressure

pipe) with no joints closer than ten feet to the other main. In all cases suitable

backfill or other structural protection shall be provided to preclude settling and/or

failure of the higher pipe.

In-line "Y" shall be installed at all service line locations in new main.

303.6	Manhole Construction

Manholes shall be constructed as indicated in the detail drawing. All manholes under

construction shall be sealed tightly to prevent storm or other non-sewage flows from

entering the sanitary sewer system. All dead-end manholes shall have line laid through

the manhole and plugged with an approved plug provided by the pipe manufacturer. If

dead-end lines are going to be temporary and are planned to be extended into future

developments, they will be plugged  with a pipe manufacturer's approved removable plug.

This plug shall be installed outside of base pour.

Sewer pipe connections to existing manholes where there is no existing pipe stubbed out

shall be made in such a manner that the finished work shall conform as nearly as

practical to the essential requirements specified for new manholes. The Responsible

Party shall break out as small an opening in the existing manhole as necessary to insert

the new sewer pipe. The existing concrete foundation bench shall be chipped to the

cross-section of the new pipe in order to form a smooth, continuous invert similar to

what would be formed in a new concrete base. Portland Cement grout shall be used as

necessary to smoothly finish the new invert and to seal the new lines so the junction

is watertight.

Top elevation of the manhole shall be adjusted to exactly match final grade prior to the

initiation of the one year warranty period. If manholes are located in open fields, they

should be left six inches to eight inches above grade where practical. A locking ring

and cover shall be installed. In cultivated areas, manholes shall be left below grade;

considering the type of equipment being used for the cultivated area, the ring and cover

elevations shall be lower in order to protect structure from damage, and properly

marked by a steel fence post painted red on the top six inches, located five feet from

the centerline of the manhole cover. Final elevation of all manholes is to be at the

discretion of the City Engineer.

303.7	Backfill

It is expected that the trench excavation shall provide suitable backfill material. Wet,

soft or frozen material, pieces of asphalt or concrete or other undesirable substances

shall not be used for backfill. The backfill material shall be free from rubbish and

stones larger than four inches in diameter, clods and frozen lumps of soil. If the

excavated material is not suitable for backfill, as determined by the Inspector, suitable

material shall be hauled in and utilized and the rejected material hauled away. All snow

shall be removed from trench prior to backfill operations.

Backfilling shall be conducted at all times in a manner to prevent damage to the pipe or

its coating and shall be kept as close to the pipe laying operation as possible.

All backfill around structures shall be consolidated by mechanical tamping.

Backfill in areas where existing pavement is to be cut and replaced, existing material

excavated shall be removed from the site and the trench backfilled with gravel road

base as specified in subsection 103.3 of these Standards and Specifications. The line,

grade and joints of all pipelines shall be inspected by the City before any back

filling above the pipe is commenced.

303.8	Compaction

Refer to subsection 204.10 of these Standards and Specifications.

303.9	Trench Maintenance

During the period of the warranty period, the Responsible Party shall maintain and repair

any trench settlement which may occur and shall make suitable repairs to any pipes,

fittings, manholes, pavement, sidewalks or other structures which may be damaged as a

result of backfill settlement as determined by the City Engineer. The Responsible Party

is also responsible for material defects.

303.10	Testing

All sanitary sewer pipe and appurtenances shall be cleaned and tested after backfill

operations have been completed and acceptable compaction test results have been

submitted to the City Engineer. If the completed line or any portion thereof fails on

any of the specified tests, the City Engineer may halt construction of any new sewer

line until such time as the previously placed sewer line meets the specifications. If

the sewer line is completed, the City Engineer may require that the Responsible Party

repair the line until it meets specifications before the line is released. The low

pressure air test along with the lamping test shall be required on the entire length

of all pipe line installations. The use of alternate testing methods may be allowed or

required in addition to those stated above and indicated by the City Engineer. Alternate

testing methods include water exfiltration test, smoke test, infiltration test,

deflection test and television inspection. After all sewer lines have been cleaned and

tested, they must be approved by the City. All work necessary to receive approval for

cleaning and testing shall be completed within 15 calendar days of backfilling.

The Responsible Party shall furnish all labor, materials, tools and equipment necessary

to clean the pipe and appurtenances, make the tests and perform all work incidental

thereto. Precautions should be taken to prevent joint drawing during the test. Any

damages to the pipeline caused by cleaning or testing operations shall be repaired or

replaced by the Responsible Party at his own expense. Should the pipeline fail to meet

these requirements, the Responsible Party shall determine the source or sources of the

leakage and shall replace all defective materials or workmanship, all at his own

expense. Pipelines which fail to meet these requirements shall be repaired or replaced

and retested in accordance with these requirements.

1.	Low Pressure Air Test

The low pressure air test shall be completed in accordance with NDEQ.

If it appears that excessive infiltration is present after the air tests have been

completed, the City Engineer may require an infiltration test prior to final

acceptance. Excessive infiltration may be the cause for rejection. The City Engineer

shall be the sole judge of whether or not the infiltration test is required.

The Responsible Party shall follow all precautions necessary to perform a safe and

successful test. Plugs used to isolate the line for the air test must be securely

braced to avoid the unintentional release of the plug. Gauges, air piping manifolds

and control valves shall be located above ground. No one shall be permitted to enter

a manhole when a plugged pipe is under pressure. Air testing apparatus shall be

equipped with a pressure relief device designed to relieve the pressure when in

excess of six p.s.i.g.

2.	Lamping Test

Prior to final acceptance of the pipeline installation, the City shall perform a

lamp test to verify the alignment and condition of the pipe. The lamp test shall

be performed after the back-fill operation has been completed and the line has been

cleaned. Scheduling of the lamp test shall be done by the Inspector. Should the

lamp test indicate an alignment problem, the City Engineer shall be the sole judge

of the need for replacement. Unsatisfactory alignment may be the cause for

rejection. The Responsible Party shall furnish the light source to be used in the

lamp test and the labor necessary for the City to perform the test.

3.	Water Exfiltration Test

The water exfiltration test shall be used only if specifically authorized by the

City Engineer. The test shall be performed after backfill operations have been

completed.

Allowable leakages shall be 50 gallons per day per inch of pipe diameter per mile

of pipeline with a minimum test pressure of 10 feet of water column above the crown

of the pipe at its midpoint of six feet above the surrounding groundwater table,

whichever causes the greater head on the pipe. The maximum allowable pressure at

any point in the pipeline during the test is a 16 foot column of water.

The Responsible Party may fill the pipe anytime up to 24 hours prior to the

performance of the test. It shall be the responsibility of the Responsible Party

to determine the level of the water table at each manhole. Unsatisfactory test

results may be the cause for rejection. The Responsible Party shall be responsible

for the repair or replacement of any portion of the pipeline which have excessive

exfiltration rates.

4.	Smoke Test

The smoke test shall be performed only if specifically authorized by the City

Engineer. The test shall be performed after backfill operations have been completed

and accepted.

The City Engineer shall supply the necessary smoke testing apparatus and shall

conduct the test after the pipeline has been cleaned and prepared by the Responsible

Party. If the tests reveal cracks or breaks in the pipeline, the City Engineer may

require additional tests or replacement. The City Engineer shall be the sole judge

of test results. Unsatisfactory results may be the cause for rejection.

5.	Infiltration Test

The water infiltration test shall be used only if specifically authorized by the

City Engineer. The test shall be performed after the backfill operations have been

completed and accepted. Allowable infiltration shall be 100 gallons per day per

inch of pipe diameter per mile of pipeline. The infiltration rate shall be measured

with a V-Notch Wier, which shall be supplied by the City Engineer. The maximum

allowable infiltration rates are identical to the maximum allowable exfiltration

rates and are as indicated in the water exfiltration test specification.

Unsatisfactory test results may be the cause for rejection. The Responsible Party

shall be responsible for the repair or replacement of any sections of pipeline

which have excessive infiltration rates.

6.	Deflection Test

The deflection test will be completed 30 days after the pipe is backfilled in

accordance with NDEQ regulations.

7.	Television Inspection

The City Engineer may require any or all sewers to be inspected by the use of a

television camera prior to final acceptance. The costs incurred in making the

inspection shall be borne by the Responsible Party. The Responsible Party shall

be responsible for all costs incurred in any television inspection performed solely

for the benefit of the Responsible Party. When television inspection is required

by the City, the Responsible Party shall perform inspection of all sewers where

directed by the City. The television shall consist of a self-contained camera and

a monitoring unit connected by a three wire coaxial cable. The camera shall be

waterproof and shall be small enough to pass unobstructed through the line being

tested.

The video equipment shall have a self continuous 650 line resolution picture showing

the entire inside periphery of the pipe. The Responsible Party shall furnish a video

tape recording of the inspection to the City on video tape which is compatible with

the existing City video equipment. The tape should be capable of sound track for

voice recording. The television inspection shall be performed on one manhole section

at a time by pulling the camera through the pipeline along its axis. Unsatisfactory

inspection results may be the cause for rejection. The Responsible Party shall be

responsible for any repairs or replacement of any portions of the pipeline which are

determined defective as a result of the television inspections.

304	SANITARY SEWER SERVICE LINES AND APPURTENANCES CONSTRUCTION SPECIFICATIONS

304.1	General

All sanitary sewer service line construction connecting to the City sanitary sewer shall

be done in accordance with these Standards and Specifications which cover all new

sanitary sewer service line construction and repairs to existing lines from the sewer

main to the building plumbing. Any deviations from these Standards and Specifications

shall be supported in writing by the City Engineer.

304.2	Materials

All materials furnished shall be new and undamaged. Everything necessary to complete

all installations shall be furnished and installed whether shown on approved drawings

or not and all installations shall be completed as fully operable.

Acceptance of materials or the waiving of inspection thereof shall in no way relieve

the Responsible Party of the responsibility for furnishing materials meeting the

requirements of the specifications.

The City of Scottsbluff reserves the right to direct or deny use of certain types of

materials in specific circumstances.

All materials delivered to the job site shall be adequately housed and protected so as

to ensure the preservation of their quality and fitness for the work.

1.	Polyvinyl Chloride Pipe

Refer to subsection 303.1(a) of these Standards and Specifications.

2.	Polyvinyl Chloride Pressure Pipe

Refer to subsection 204.1(b) of these Standards and Specifications.

3.	Manholes

Refer to subsection 303.1(c) of these Standards and Specifications.

304.3	Excavation

Refer to subsection 303.2 of these Standards and Specifications.

304.4	Dewatering

Refer to subsection 303.3 of these Standards and Specifications.

304.5	Pipe Bedding

Refer to subsection 303.4 of these Standards and Specifications.

All specifications are applicable except that four inch and six inch service lines

require a minimum bedding depth of eight inches as shown in the detail drawing.

304.6	Installation of Pipe

Refer to subsection 303.5 of these Standards and Specifications.

304.7	Manhole Construction

Refer to subsection 303.6 of these Standards and Specifications.

304.8	Backfill

Refer to subsection 303.7 of these Standards and Specifications.

304.9	Compaction

Refer to subsection 204.10 of these Standards and Specifications.

304.10	Location and Alignment of Service

Sanitary sewer service lines shall be constructed on the shortest and straightest route

possible. At no time shall the service line be any closer than five feet to the side

property line, and no service line may be constructed through or in front of any

adjoining property. When possible, the service line shall be located five feet toward

the low side of the lot from the centerline of the lot. Service lines are not to

extend beneath driveways. If a sanitary sewer line must extend beneath a driveway, a

variance must be granted by the City Engineer. Sewer and water service lines must be a

minimum of 10 feet apart horizontally or concrete encasement of the sewer line or

special protection shall be required. Refer to subsection 303.5 of these Standards and

Specifications for additional information.

304.11	Service Stub-Ins to Property Line

Service stub-ins shall be extended at least to property line and shall be plugged with a

watertight compression stop. Adjacent to the end of the stub-in, a four foot length of

two-inch by four-inch wood marker (or a four-foot length steel fence post) shall be

placed in a vertical position prior to backfilling. The Responsible Party shall place a

chiseled (X) in the curb head to the location where the service line crosses underneath

the curb. This two-inch by four-inch shall remain in place until service locations are

chiselled on the curb. If the two-inch by four-inch wood marker is not present at time

of chiselling, the Responsible Party shall bear the expense of reaffirming the location

of the service stub out out by reexcavation. The Responsible Party shall take

measurements of distances from manholes to service taps and give this information to the

City. Service locations for sanitary sewer shall also be marked with an "X" on the curb.

Markings shall be neatly chiselled, or saw-cut, not painted by the Responsible Party.

304.12	Connections

Where wyes have not or could not have been installed in the main sewer, the Responsible

Party shall excavate around the main and prepare the main for tapping. The main shall

then be tapped by the Responsible Party. The connections shall be watertight and at a 45

degree angle above the pipe horizontal centerline. No projection of the sewer service

pipe inside the sewer main being connected to shall be permitted. Approved tees or sewer

service saddles shall be used to connect the service line to the sewer main. After

completion of the sewer tap, pipe laying and all other work shall be performed by the

Responsible Party.

No aluminum saddles shall be permitted. Plastic saddles shall be attached to the mains

utilizing either epoxies or stainless steel straps. The City shall inspect the main and

saddles at every tap prior to backfilling. In the event the tap is covered before it is

inspected, it shall be dug out by the Responsible Party and any concrete or mortar

around the fitting shall be removed to allow visual inspection of the tap and the main.

If the main sewer line is cracked or broken during the process of locating and tapping,

it shall be repaired immediately either by replacing the broken section or by placing

a minimum of nine inches of concrete above, at the sides and below the main pipe

parallel for the width of the excavation. The method of repair shall be chosen by the

Inspector. Lines in service must be machine tapped. Two machine taps on the same joint

of pipe shall not be permitted.

A manhole shall be installed instead of a service tap when a six inch connection is to

be made on an existing eight-inch or ten-inch line. Six-inch connections may be made

without a manhole on new line installations with the use of a wye. If a wye cannot be

used, a manhole shall be required on eight-inch and ten-inch new lines. Service taps

to existing manholes shall not be permitted, unless otherwise authorized by the City

Engineer.

Sewer mains shall be laid through manholes at the end of cul-de-sacs. One joint of

pipe and plugged wyes shall be installed in order that the end of the cul-de-sac may

be serviced without tapping into the manhole. No more than two wyes may be located

on that joint of pipe laid through the manhole.

No more than three one-quarter bends shall be permitted in any sanitary sewer line.

Where service lines are longer than 100 feet, cleanouts shall be required.

304.13	Commercial and/or Industrial Manholes

A manhole may be required where so specified by the City Engineer in order to have

samples taken if industrial wastes are suspected. Such a manhole would be located on

the commercial service line, so samples could be taken before such fluids could reach

the sanitary sewer main line.

304.14	Infiltration

The joints shall be made in a workmanlike manner so as to ensure a maximum infiltration

of not more than 0.032 gallons per inch of diameter per hour per 100 feet.

Service lines to be abandoned shall be dug and plugged at the main with an approved

watertight compression stop, unless otherwise specified.

SECTION 400

STORM DRAINAGE DESIGN AND TECHNICAL CRITERIA

SECTION 400 - STORM DRAINAGE DESIGN AND TECHNICAL CRITERIA

TABLE OF CONTENTS			PAGE

401	GENERAL PROVISIONS		400-1

401.1	Review Process		400-1

401.2	Drainage Report		400-1

SECTION 400 - STORM DRAINAGE DESIGN AND TECHNICAL CRITERIA

401	RENERAL PROVISIONS

401.1	Review Process

All subdivision, zoning and site development within the City require drainage reports,

construction drawings/specifications, and record drawing information be submitted in

accordance with the requirements of Section 100 and 400 of these Standards and

Specifications. All submitted reports should be clearly and cleanly reproduced.

Photostatic copies of charts, tables, nomographs, calculations, or any other referenced

material shall be legible. Washed out, blurred, or unreadable portions of the report are

unacceptable and could warrant resubmittal of the report. The submittal shall include a

declaration of the method used for design of the drainage report. The drainage report

shall be based on runoff coefficients for complete development within the proposed zone

or site. Incomplete or absent information may result in the report being rejected for

review. The City Engineer may, at his/her discretion, waive the requirements for a

drainage report. Drainage reports shall utilize the most recent City storm sewer report

and supplement flow data from the report.

The City shall make every effort to effect a complete review and comment in a timely

fashion. However, the City Engineer cannot approve reports or plans by default, nor can

the City Engineer guarantee the time for review.

401.2	Drainage Report

The drainage report shall be based on the rational method for small drainage areas (less

than 200 acres), and the SCS or other approved methods for large drainage areas. The

report shall be submitted by a professional engineer and inlet structure design shall

comply with NDOR standards, City of Scottsbluff standards or prior approved standards.

Minimum design storm shall be 10 years, but may be increased at the direction of the

Planning and Building Official, when area concerns dictate, or as directed by the Storm

Water Master Plan.

SECTION 400 - STORM DRAINAGE DESIGN AND TECHNICAL CRITERIA

TABLE OF CONTENTS

PAGE

401	GENERAL PROVISIONS		400-1

401.1	Purpose			400-1

401.2	Review and Approval		400-1

401.3	Interpretation		400-1

401.4	Relationship to Other Standards		400-1

402	DRAINAGE PLANNING SUBMITTAL REQUIREMENTS		400-1

402.1	Review Process		400-1

402.2	Phase I Drainage Report		400-2

402.3	Phase II Drainage Report		400-4

402.4	Phase III Drainage Report		400-8

402.5	Construction Plans		400-9

402.6	Record Drawings and Final Acceptance Certificate	400-10

403	DRAINAGE POLICY			400-11

403.1	Introduction		400-11

403.2	Basic Principles		400-11

403.3	Regional and Local Planning		400-12

403.4	Technology Planning and Design		400-16

403.5	Irrigation Facilities		400-19

404	RAINFALL				400-20

404.1	Introduction		400-20

404.2	CUHP Design Storms		400-20

404.3	Time-Intensity-Frequency Curves		400-21

405	RUNOFF					400-21

405.1	Introduction		400-21

405.2	Rational Method		400-21

405.3	Colorado????? Urban Hydrograph Procedure	400-22

405.4	Storm Flow Analysis		400-22

405.5	On-Site Flow Analysis		400-22

405.6	On-site Flow Analysis		400-22

405.7	Tributary Area within a Major Drainageway Basin	400-22

405.8	Tributary Area Not Within a Major Drainageway Basin	400-23

405.9	CUHP Computer Program		400-23

406	OPEN CHANNELS			400-23

406.1	Introduction		400-23

406.2	Channel Types		400-23

406.3	Flow Computation		400-26

406.4	Design Standards for Major Drainageways	400-26

406.5	Design Standards for Small Drainageways	400-33

406.6	Roadside Ditches		400-39

406.7	Channel Rundowns		400-40

406.8	Checklist			400-41

407	STORM SEWERS			400-41

407.1	Introduction		400-41

407.2	Construction Materials		400-41

407.3	Hydraulic Design		400-42

407.4	Vertical Alignment		400-44

407.5	Horizontal Alignment		400-45

407.6	Pipe Size			400-45

407.7	Manholes			400-45

407.8	Design Example		400-45

407.9	Checklist			400-49

408	STORM SEWER INLETS		400-49

408.1	Introduction		400-49

408.2	Standard Inlets		400-49

408.3	Inlet Hydraulics		400-50

408.4	Inlet Spacing		400-52

408.5	Checklist			400-53

409	STREETS				400-54

409.1	Introduction		400-54

409.2	Function of Streets in the Drainage System	400-54

409.3	Street Classification		400-54

409.4	Hydraulic Evaluation		400-54

409.5	Design Example		400-55

409.6	Checklist			400-56

410	CULVERTS				400-56

410.1	Introduction		400-56

410.2	Culvert Hydraulics		400-56

410.3	Culvert Design Standards		400-57

410.4	Design Example		400-61

410.5	Culvert Sizing Criteria		400-64

410.6	Checklist			400-65

411	HYDRAULIC STRUCTURES		400-65

411.1	Erosion Control		400-65

411.2	Riprap			400-65

411.3	Energy Dissipators		400-65

411.4	Check Structures		400-65

411.5	Bridges			400-66

411.6	Irrigation Ditch Crossings		400-66

412	CONTROL OF EROSION & SEDIMENTATION FROM CONSTRUCTION	400-66

412.1	Introduction		400-66

412.2	Standards and Requirements		400-67

413	DETENTION				400-72

413.1	Introduction		400-72

413.2	Detention Methods		400-72

413.3	Design Criteria		400-72

413.4	Design Standards for Open Space Detention	400-74

413.5	Design Standards for Parking Lot Detention	400-76

413.6	Design Standards for Underground Detention	400-77

413.7	Design Examples		400-78

314.8	Checklist			400-81

TABLES

400-1	Required Operations and Maintenance Easement	400-15

400-2	Recurrence Interval		400-17

400-3	Allowable Use of Streets for Major Storm Runoff	400-17

400-4	Allowable Use of Streets for Major Storm Runoff	400-18

400-5	Allowable Cross Street Flow		400-18

400-6	Allowable Culvert Overtopping		400-19

400-7	Storm Sewer Standards		400-41

400-8	Standard Inlet Type		400-49

400-9	Allowable Inlet Capacity		400-50

400-10	Criteria for Final Erosion Control and Submittal	400-68

400-11	Allowable Release Rates for Detention Ponds	400-73

400-12	Maintenance Access Requirements		400-78

FIGURES

400-1	Storm Drainage Analysis Submittals

400-2	Floodplain Information for the City of Scottsbluff

400-3	Floodplain Information for the City of Scottsbluff (continued)

400-4	Drawing Symbol Criteria and Hydrology Review Table

400-5	Submittal/Review Process

400-6	Floodplain Information for the City of Scottsbluff

400-7	Roughness Coefficient for Grassed Channels

400-8	Typical Grassed Lined Channel Section

400-9	Typical Grassed Lined Channel Section

400-10	Typical Grassed Lined Channel Section

400-11	Roadside Ditch Sections

400-12	Trickle Channel Details

400-13	Channel Rundown Detail

400-14	Storm Sewer Alignment and Size Criteria

400-15	Storm Sewer Energy Loss Coefficient

400-16	Storm Sewer Energy Loss Coefficient

400-17	Storm Sewer Energy Loss Coefficient

400-18	Manhole and Junction Losses

400-19	Design Example for Storm Sewers

400-20	Hydraulic Properties Circular Pipe

400-21	Hydraulic Properties Horizontal Elliptical Pipe

400-22	Hydraulic Properties Arch Pipe

400-23	Design Example for Storm Sewers - Plan

400-24	Design Example for Storm Sewers - Profile

400-25	Allowable Inlet Capacity

400-26	Allowable Inlet Capacity

400-27	Allowable Inlet Capacity

400-28	Inlet Design Examples Minor Storm

400-29	Nomograph for Flow in Triangular Gutters

400-30	Gutter Capacity Reduction Curves

400-31	Allowable Gutter Capacity

400-32	Allowable Gutter Capacity

400-33	Gutter Capacity Adjustment

400-34	Hydraulic Data for Culverts

400-35	Hydraulic Data for Culverts

400-36	Mean Annual Flood for Low Water Crossing Computations

400-37	Example of Standard Form SF-10

400-38	Low Water Crossing Example No. 6

400-39	USBR Type-VI Stilling Basin

400-40	Erosion Control Plan (ECP) Submittal Requirements

400-41	Weir Flow Coefficients

400-42	Detention Pond Outlet Configuration

400-43	Detention Pond Details

400-44	Weir Design Example

400-45	Underground Detention

400-46	Outlet Design Example

400-47	Typical Erosion Control Mattresses

400-48	Roadside Ditch Capacities

400-49	Design Storms for the City of Scottsbluff

400-50	Time-Intensity-Frequency Curves

400-51	Time-Intensity-Frequency Tabulation

400-SFI Drainage Report Submittal Checklist

400-SF2 Time of Concentration

400-SF3 Storm Drainage System Design

400-SF4 Culvert Rating

SECTION 400 - STORM DRAINAGE DESIGN AND TECHNICAL CRITERIA

401.1	Purpose

This section presents the minimum design and technical criteria for the analysis and

design of storm drainage facilities. All subdivision, zoning, and other proposed site

development submitted for approval under the provisions of the Code shall include

adequate storm drainage system analysis and appropriate drainage system design. Such

analysis and design shall meet or exceed these Standards and Specifications. Policies

and technical criteria not specifically addressed in this document shall follow the

provisions of the Urban Drainage and Flood Control District (UD&FCD) Urban Storm

Drainage Criteria Manual (UD&FCD Manual). The applicant is also referred to the

Nebraska Department of Transportation's Standard Plans ("M-Standards") for additional

design details not covered in these Standards and Specifications or the UD&FCD Manual.

Drainage facilities currently in place or under construction shall be accepted without

regard to the provisions of these criteria.

401.2	Review and Approval

The City Engineer shall review all drainage submittals as necessary for general

compliance with these Standards and Specifications (see Figure 400-5). An approval by

the City engineer does not relieve the Responsible Party from the responsibility of

ensuring that the calculations, plans, specifications, construction, and record drawings

are in compliance with these Standards and Specifications.

The City Engineer may request the UD&FCD review reports and construction plans required

by this Section 400 or the UD&FCD Manual. Where major drainageway improvements or

floodplain delineation are involved, UD&FCD approval may be required.

401.3	Interpretation

In the interpretation and application of the provisions of these criteria, the following

shall govern:

In its interpretation and application, the provisions shall be regarded as the minimum

requirements for the protection of the public health, safety, comfort, morals,

convenience, prosperity, and welfare of the residents of the City.

These Standards and Specifications shall not abrogate or annul any permits or approved

drainage reports and construction plans within one year prior to the effective date of

these Standards and Specifications or any easement or covenant.

401.4	Relationship to Other Standards

These Standards and Specifications are consistent with the UD&FCD criteria. If the state

or federal government imposes more strict criteria, or requirements (as decided by the

City Engineer), these shall be incorporated into the City's requirements after due

process and public hearing(s) needed to modify the City's regulations and standards.

402	DRAINAGE PLANNING SUBMITTAL REQUIREMENTS

402.1	Review Process

All subdivision, zoning and site development within the City require drainage reports,

construction drawings/specifications, and record drawing information be submitted in

accordance with the requirements of Sections 100 and 400 of these Standards and

Specifications. All submitted reports should be clearly and cleanly reproduced.

Photostatic copies of charts, tables, nomographs, calculations, or any other referenced

material shall be legible. Washed out, blurred, or unreadable portions of the report

are unacceptable and could warrant resubmittal of the report. The submittal shall include

a declaration of the type of report submitted (i.e., Phase-I, Phase-II, or Phase-III).

Standard Form SF-1 shall be used to determine the adequacy of the submittal. Incomplete

or absent information may result in the report being rejected for review. The City

Engineer may, at his/her discretion, allow Phase I, II, and/or III reports consolidated

into a single or dual report if the area in question is smaller in size than five acres.

The City shall make every effort to effect a complete review and comment in a timely

fashion. However, the City Engineer cannot approve reports or plans by default, nor can

the City Engineer guarantee the time for review.

402.2	Phase I Drainage Report

The Phase I Drainage Report is the first step in the approval process. Refer to Figure

400-1 to determine which types of development require a Phase I submittal. This report

shall review at a conceptual level the feasibility and design characteristics of the

proposed development. The Phase I drainage report shall be in accordance with the

following outline and contain the applicable information listed:

(a)	Report Contents

I. GENERAL LOCATION AND DESCRIPTION

A. Location

1. City, County, State Highway and local streets within and adjacent to

the site, or the area to be served by the drainage improvements

2. Township, range, section, 1/4 section

3. Major drainageways and facilities

4. Names of surrounding developments

B. Description of Property

1. Area in acres

2. Ground cover (type of ground cover and vegetation)

3. Major drainageways

4. Existing major irrigation facilities such as ditches and canals

5. Proposed land use

6. Floodplain status

II.	DRAINAGE BASINS AND SUB-BASINS

A. Major Basin Description

1. Reference to major drainageway planning studies such as flood hazard

delineation report, major drainageway planning reports, and flood

insurance rate maps (see Figure 400-2, 400-3, and 400-6)

2. Major basin drainage characteristics, existing and planned land

uses within the basin, as defined by the Planning Department

3. Identification of all nearby irrigation facilities within 100-feet

of the property boundary, which shall influence or be influenced by

the local drainage.

B. Sub-Basin Description

1. Discussion of historic drainage patterns of the property in question

2. Discussion of off-site drainage flow patterns and impact on development

under existing and fully developed basin conditions as defined by the

Planning Department

III.	DRAINAGE FACILITY DESIGN

A. General Concept

1. Discussion of concept and typical drainage patterns

2. Discussion of compliance with off-site runoff consideration

3. Discussion of anticipated and proposed drainage patterns

4. Discussion of the content of tables, charts, figures, plates, or

drawings presented in the report

B. Specific Details (Optional Information)

1. Discussions of drainage problems encountered and solutions at specific

design points

2. Discussion of detention storage and outlet design

3. Discussion of maintenance and access aspects of the design

4. Discussion of impacts of concentrating the flow on the downstream

properties

IV.	WETLAND DETERMINATION AND REVIEW

V.	REFERENCES

Reference all criteria, master plans, and technical information used in

support of concept.

(b)	Drawing Contents

1.	General Location Map: All drawings shall be 24 inches x 36 inches in size. A

map shall be provided in sufficient detail to identify drainage flows entering

and leaving the development and general drainage patterns. The map should

generally be at a scale of 1" = 100' to 1" = 400' and show the path of all

drainage from the upper end of any off-site basins to the defined major

drainageways (see Figure 404). The map shall identify any major facilities

from the property (i.e., development, irrigation ditches, existing detention

facilities, culverts, storm sewers) along the flow path to the nearest major

drainageway.

Basins and divides are to be identified and topographic contours are to be

included.

2.	Floodplain Information: A copy of Figure 400-6 showing the location of the

subject property shall be included with the report as outlined in subsection

402.2(a), above. All major drainageways (see subsection 403.2(e)) shall have

the flow path defined and shown on the report drawings.

3.	Drainage Plan: Map(s) of the proposed development at a scale of 1" = 20' to

1" = 200' on a 24 inch x 36 inch drawing shall be included. The plan shall

show the following:

a. Existing topographic contours at two foot maximum intervals. In terrain

where the slope exceeds 15 percent, the maximum interval is 10-feet.

The contours shall extend a minimum of 100-feet beyond the property

lines.

b. All existing drainage facilities.

c. Approximate flooding limits based on available information, such as

previously defined floodplains and estimated floodplains.

d. Conceptual major drainage facilities including detention basins, storm

sewers, swales, riprap, and outlet structures in the detail consistent

with the proposed development plan.

e. Major drainage boundaries and sub-boundaries.

f. Any off-site feature influencing development.

g. Proposed flow directions and, if available, proposed contours.

h. Legend to define map symbols (see Figure 400-4).

i. Title block in lower right corner.

402.3	Phase II Drainage Report

The purpose of the Phase II Drainage Report is to identify and refine conceptual

solutions to the problems which may occur on-site and off-site because of the

development. Refer to Figure 400-1 to determine which types of development require a

Phase II submittal. In addition, those problems that exist on site before development

must be addressed during the preliminary phase. All reports shall be typed on 8-1/2

inches x 11 inches paper and bound. The drawings, figures, plates, and tables shall be

bound with the report or included in a pocket attached to the report. The report shall

include a cover letter presenting the preliminary design for review and shall be prepared

by or supervised by an engineer licensed in Nebraska. The report shall contain a

certification sheet as follows:

"I hereby certify that this report (plan) for the Phase II drainage design of (Name of

Development) was prepared by me (or under my direct supervision) in accordance with the

provisions of the City of Scottsbluff Storm Drainage Design and Technical Criteria for

the Responsible Parties thereof. I understand that the City of Scottsbluff does not and

shall not assume liability for drainage facilities designed by others."

Registered Professional Engineer

State of Nebraska No.

(Affix Seal)

(a)	Report Contents

The Report shall be in accordance with the following outline and contains the

applicable information listed:

I.   GENERAL LOCATION AND DESCRIPTION

A. Location

1. Township, range, section, 1/4 section.

2. Streets within and adjacent to the subdivision with ROW width shown.

3. Major drainageways, facilities, and easements within and adjacent to

the site.

4. Names of surrounding developments.

B. Description of Property

1. Area in acres.

2. Ground cover (type of trees, shrubs, vegetation, general soil

conditions, topography, and slope).

3. Major drainageways.

4. General project description.

5. Irrigation facilities.

6. Proposed land use.

II.  DRAINAGE BASINS AND SUB-BASINS

A. Major Basin Description

1. Reference to major drainageway planning studies such as flood

hazard delineation reports, major drainageway planning reports, and

flood insurance rate maps (see Figure 400-2, 400-3, and 400-6).

2. Major basin drainage characteristics, existing and planned land

uses.

3. Identification of all irrigation facilities within the basin which

shall influence or be influenced by the local drainage.

B. Sub-Basin Description

1. Discussion of historic drainage patterns of the property in

question.

2. Discussion of off-site drainage flow patterns and impact on

development under existing and fully developed basin conditions,

as defined by the Planning Department.

III. DRAINAGE DESIGN CRITERIA

A. Regulations: Discussion of the optional provisions selected or the

deviation from the criteria, if any, and its justification.

B. Development Criteria Reference and Constraints

1. Discussion of previous drainage studies (i.e., project master

plans) for the site in question that influence or are influenced

by the drainage design and how the plan shall affect drainage

design for the site.

2. Discussion of the effects of adjacent drainage studies.

3. Discussion of the drainage impact of site constraints such as

streets, utilities, light rail rapid transit, existing structures,

and development or site plan.

C. Hydrological Criteria

1. Identify design rainfall.

2. Identify runoff calculation method.

3. Identify detention discharge and storage calculation method.

4. Identify design storm recurrence intervals.

5. Discussion and justification of other criteria or calculation

methods used that are not presented in or referenced by the

criteria.

D. Hydraulic Criteria

1. Identify various capacity references.

2. Discussion of other drainage facility design criteria used that

are not presented in the criteria.

E. Variances from Criteria

1. Identify provisions by section number for which a variance is

requested.

2. Provide justification for each variance requested.

IV.  WETLAND PRESERVATION AND MITIGATION

V.   DRAINAGE FACILITY DESIGN

A. General Concept

1. Discussion of concept and typical drainage patterns.

2. Discussion of compliance with off-site runoff considerations.

3. Discussion of the content of tables, charts, figures, plates, or

drawings presented in the report.

4. Discussion of anticipated and proposed drainage patterns.

B. Specific Details

1. Discussion of drainage problems encountered and solutions at

specific design points.

2. Discussion of detention storage and outlet design.

3. Discussion of maintenance access and aspects of the design.

4. Discussion of easements and tracts for drainage purposes, including

the conditions and limitations for use.

VI.  CONCLUSIONS

A. Compliance with Standards

1. "Criteria".

2. "Major Drainageway Planning Studies".

3. "UD&FCD Manual".

B. Drainage Concept

1. Effectiveness of drainage design to control damage from storm

runoff.

2. Influence of proposed development on the Major Drainageway

Planning Studies recommendation(s).

VII. REFERENCES

Reference all criteria and technical information used.

VIII.APPENDICES

A. Hydrologic Computations

1. Land use assumptions regarding adjacent properties.

2. Initial and major storm runoff at specific design points.

3. Historic and fully developed runoff computations at specific

design points.

4. Hydrographs at critical design points.

5. Time of concentration and runoff coefficients for each basin.

B. Hydraulic Computations

1. Culvert capacities.

2. Storm sewer capacity, including energy grade line (EGL) and

hydraulic grade line (HGL) elevations for culverts 30 inches

or larger.

3. Gutter capacity as compared to allowable using Figures 400-31 and

400-32.

4. Storm inlet capacity including inlet control rating at connection

to storm sewer.

5. Open channel design.

6. Check and/or channel drop design.

7. Detention area/volume capacity and outlet capacity.

8. Downstream/outfall system capacity to the Major Drainageway System.

(b)	Drawings Contents

1.	General Location Map: All drawings shall be 24 inches x 36 inches in size. A

map shall be provided in sufficient detail to identify drainage flows entering

and leaving the development and general drainage patterns. The map should be at

a scale of 1" = 100' to 1" = 400' and show the path of all drainage from the

upper end of any off-site basins to the defined major drainageways (see Figure

400-6 and Drainage Policy). The map shall identify any major construction

(i.e., development, irrigation ditches, existing detention facilities,

culverts, storm sewers) along the entire path of drainage. Basins and divides

are to be identified and topographic contours are to be included.

2.	Floodplain Information: A copy of Figure 400-6 showing the location of the

subject property shall be included with the report. All major drainageways

(see subsection 403.2(e)) shall have the flow path defined and shown on the

report drawings.

3.	Drainage Plan: Map(s) of the proposed development at a scale of 1" = 20' to

1" = 200' on a 24 inches x 36 inches drawing shall be included. The plan shall

show the following:

a. Existing and proposed contours at 2-feet maximum intervals. The contours

shall extend a minimum of 100-feet beyond the property lines.

b. Property lines and easements with purposes noted.

c. Streets, indicating ROW width, flowline width, curb type, sidewalk, and

approximate slopes.

d. Existing drainage facilities and structures, including irrigation ditches,

roadside ditches, crosspans, drainageways, gutter flow directions, and

culverts. All pertinent information such as material, size, shape, slope,

and location shall also be included.

e. Over-all drainage area boundary and drainage sub-area boundaries.

f. Proposed type of street flow (i.e., vertical or combination curb and

gutter), roadside ditch, gutter, slope and flow directions, and cross pans.

g. Proposed storm sewers and open drainageways, including inlets, manholes,

culverts, and other appurtenances, including riprap protection.

h. Proposed outfall point for runoff from the developed area and facilities

to convey flows to the final outfall point without damage to downstream

properties.

i. Routing and accumulation of flows at various critical points for the initial

storm runoff listed on the drawing using the format shown in Figure 400-4.

j. Routing and accumulation of flows at various critical points for the major

storm runoff listed on the drawing using the format shown in Figure 400-4.

k. Volumes and release rates for detention storage facilities and information

on outlet works.

l. Location and elevations of all existing floodplains affecting the property.

m. Location and elevations of all existing and proposed utilities affected by

or affecting the drainage design by reference to USGS and City of

Scottsbluff datum.

n. Routing of off-site drainage flow through the development and to a major

drainageway.

o. Definition of flow path leaving the development through the downstream

properties ending at a major drainageway.

p. Legend to define map symbols (see Figure 400-4 for symbol criteria).

q. Title block in lower right corner.

402.4	Phase III Drainage Report

The purpose of the Phase III Drainage Report is to update the concepts, and to present

the design details for the drainage facilities discussed in the Phase II Drainage

Report. Also, any change to the Phase II concept must be presented.

The Phase III Drainage Report shall be submitted with the application for final plat.

This requirement applies when the preliminary plat has been approved by the City

Council prior to submittal of the final plat application. If the preliminary and final

plat applications are submitted concurrently, the submittal requirements of subsection

402.4 (Phase III Drainage Report) shall apply. The Phase III Report (which updates the

Phase II Report) must be reviewed with the submittal of the construction plans and

approved by the City Engineer prior to scheduling any construction.

All reports shall be typed on a 8-1/2 inches x 11 inches paper and bound. The drawings,

figures, charts, plates and/or tables shall be bound with the report or included in a

folder/pocket attached at the back of the report.

The report shall include a cover letter presenting the final design for review and shall

be prepared by or under the direction of an engineer licensed in Nebraska, certified as

shown above in subsection 402.3 for the Phase II report. The report also shall contain a

Responsible Party certification sheet as follows:

"(Name of Responsible Party) hereby certifies that the drainage facilities for (Name of

Development) shall be constructed according to the design presented in this report. I

understand that the City of Scottsbluff does not and shall not assume liability for the

drainage facilities designed and/or certified by my engineer. I understand that the City

of Scottsbluff reviews drainage plans but cannot, on behalf of (Name of Development),

guarantee that final drainage design review shall absolve (Name of Responsible Party)

and/or their successors and/or assigns of future liability for improper design. I

further understand that approval of the Final Plat and/or Final Development Plan does not

imply approval of my engineer's drainage design."

Attest

Name of Responsible Party

Notary Public	Authorized Signature

The Phase III Drainage Report shall be prepared in accordance with the outline shown in

subsection 402.3(a). The report drawings shall follow the requirements presented in

subsection 402.3(b), above.

A mylar reproducible of the approved Phase III Drainage Plan shall be submitted to the

City Engineer for signature and retention in their files. A copy of the approved plan

shall be returned to the applicant.

402.5	Construction Plans

Where drainage improvements are to be constructed, the preliminary construction plans

(on 24 inches x 36 inches mylar) shall be submitted with the Phase III Drainage Report.

Final construction plans must be submitted at least four weeks before anticipated

issuance of construction permits for the public improvements covered by the plan.

Approval of the final construction plans by the City Engineer is a condition of the

City for issuing the construction permits. A mylar reproducible and four sets of prints

of the approved Phase III Drainage Plan shall be submitted to the City Engineer for

approval and signature. The plans for the drainage improvements shall include:

1.	Storm sewers, inlets, outlets and manholes with pertinent elevations, dimensions,

type, and horizontal control indicated.

2.	Culverts, end sections, and inlet/outlet protection with dimensions, type,

elevations, and horizontal control indicated.

3.	Channels, ditches, and swales (including side/rear yard swales) with lengths,

widths, cross-sections, and erosion control (i.e., riprap, concrete, grout)

indicated.

4.	Checks, channel drops, erosion control facilities.

5.	Detention pond grading, trickle channels, outlets, and landscaping.

6.	Other drainage related structures and facilities (including underdrains and sump

pump lines).

7.	Maintenance access considerations.

8.	Overlot grading and erosion and sedimentation control plan (refer to section 413).

9.	FHA/VA final lot grading requirements (separate attachments).

10.	Tabulation of quantities (may be submitted separately).

11.	Offsite routing and easements.

The information required for the plans shall be in accordance with sound engineering

principles, these criteria and the City requirements for subdivision designs.

Construction documents shall include geometric, dimensional, structural, foundation,

bedding, hydraulic, landscaping, and other details as needed to construct the storm

drainage facility. The approved Phase III Drainage Plan shall be included as part of

the construction documents for all facilities affected by the drainage plan. Construction

plans shall be signed by a Nebraska registered professional engineer as being in

accordance with the City Engineer approved drainage report/drawings.

402.6	Record Drawings and Final Acceptance Certificate

Record drawings for all improvements are to be submitted to the City with the request for

Final Acceptance. Certification of the record drawings is required as follows:

1.	Registered Land Surveyor: A registered land surveyor in the State of Nebraska shall

certify the as-built detention pond volumes and surface areas at the design depths,

outlet structure sizes and elevations, storm sewer sizes and invert elevations at

inlets, manholes, and discharge location, and representative open channel cross-

sections, and dimensions of all the drainage structures.

2.	Registered Professional Engineer: The responsible engineer shall state that "to the

best of my knowledge, belief, and opinion, the drainage facilities were constructed

in accordance with the design intent of the approved drainage report and

construction drawings" in accordance with State Law. The Professional Engineer shall

sign each blueprint. The mylar shall state the date the Professional Engineer signed

the blueprints and that they are on file.

The certified record drawings shall be submitted as mylars.

The City Engineer shall compare the certified record drawing information with the

construction drawings. A Final Acceptance Certificate shall be issued only if:

1.	The record drawing information demonstrates that the construction is in compliance

with the design intent.

2.	The record drawings are certified by both a Professional Land Surveyor and a

Professional Engineer, both registered in the State of Nebraska.

A summary of the required certifications and approvals is presented below.

CITY

CERTIFICATION                    APPROVAL

ITEM                    REQUIRED                         REQUIRED

Phase I Report          None                             Yes

Phase II Report         Professional Engineer            Yes

Phase III Report        Professional Engineer            Yes

Responsible Party

Construction Drawings   Professional Engineer            Yes

Record Drawings         Professional Engineer            Yes

Professional Land Surveyor       (Final Acceptance)

403	DRAINAGE POLICY

403.1	Introduction

The provisions for adequate drainage in urban areas is necessary to preserve and promote

the general health, welfare, and economic well being of the region. Drainage is a

regional feature that affects all governmental jurisdictions and all parcels of property.

This characteristic of drainage makes it necessary to formulate a program that balances

both public and private involvement. Overall coordination and master planning must be

provided by the governmental units most directly involved, but drainage must be

integrated on a regional level.

403.2	Basic Principles

(a)	Urban Sub-System

Drainage is a sub-system of all urbanization. The planning of drainage facilities

must be included in the urbanization process. The first step is to include drainage

planning with all regional and local development master plans. The report shall

address multiple purpose use of land for drainage and open space.

Storm water management facilities, such as channels and storm sewers, serve both a

conveyance and storage function. When a channel is planned as a conveyance feature,

it requires an outlet as well as downstream storage space. When the space

requirements are considered, the provision for adequate drainage becomes a competing

use for space along with other land uses. If adequate provision is not made in a

land use plan for the drainage requirements, storm water runoff shall conflict with

other land uses and shall result in water damages, and shall impair or even disrupt

the functioning of other urban systems.

(b)	Multi-Purpose Resource

Storm water runoff is an urban resource. Whereas the runoff can be a liability to

urbanization, storm runoff has potential for beneficial use. This use, however, must

be compatible with adjacent land uses and Nebraska Water Law.

When storm water runoff is treated as a resource, quality aspects of the water

become important. This in turn relates to issues such as street cleaning practices,

solid waste collection and removal services, and regulations on the development of

raw land to control erosion and resulting silt loads. These practices influence

succeeding water uses.

The storm water urban sub-system should be multi-purpose to satisfy the competing

demands placed on water within the urban environment. Drainage facilities can

fulfill other purposes besides just drainage; and facilities not designed

primarily for drainage frequently can be designed to provide drainage benefits.

(c)	Water Rights

When the drainage sub-system interferes with existing water rights, the value and

use of the water are affected. The existing drainageways and storage locations

frequently interrelate with the water rights, which must be addressed when

planning the facility to preserve their integrity.

Ditches which have direct flow rights from a stream are controlled by headgates.

Drainage improvements, which alter the quantity (or quality) of the water

available to the headgate, affect the ability to divert water. Other ditches

obtain all or portions of the rights by intercepting the shallow groundwater

(seepage right). If the water right has not been abandoned or transferred to

another location, the drainage design (including the sub-surface system) must be

planned and constructed to preserve the water right. Similar situations also can

occur when planning drainage facilities near reservoirs.

(d)	Jurisdictional Boundaries

Since drainage considerations and problems are regional in nature, and do not

respect jurisdictional boundaries, a successful plan must emphasize regional

cooperation in accomplishing the goals.

(e)	Major Drainageway

For the purpose of these Standards and Specifications, a Major Drainageway

shall be defined as any drainage flow path with a tributary area of 130 acres or

more.

403.3	Regional and Local Planning

(a)	Basin Transfer

Nebraska drainage law recognizes the inequitability of transferring the burden on

managing storm drainage from one location or property to another. Liability

questions also arise when the historic drainage continuum is altered. The diversion

of storm runoff from one basin to another should be avoided unless specific and

prudent reasons justify and dictate such a transfer. Prior to selecting a solution,

alternatives should be reviewed. Planning and design of storm water drainage

systems should not be based on the premise that problems can be transferred from'

one location to another.

The subdivision process can and shall significantly alter the historic or natural

drainage paths. When these alterations result in a subdivision outfall system that

discharges back into the natural drainageway at or near the historic location,

then the alterations (intra-basin transfer) are generally acceptable. However,

when the subdivision outfall system does not return to the historic drainageway,

then inter-basin transfer may result. This inter-basin transfer should be

prevented since it violates a basic civil drainage law principle by discharging

water onto a subservient property in a manner or quantity to do more harm than

formerly. If the development significantly increases the drainage area tributary

to the subdivision outfall, then inter-basin transfer into the property has

occurred, which also must be prevented.

(b)	Master Planning

As set forth in subsection 403.2(a) drainage planning is required for all new

development plans. In recognition that drainage boundaries are non-jurisdictional,

the City has participated in regional basin wide master plans to define the Major

Drainageway Facilities. The City shall also encourage and participate in future

master plans.

City encourages the development of detailed regional drainage master plans which

shall set forth site requirements for new development and identify the required

public improvements. Master plans shall be approved and adopted. Areas proposed

for annexation not presently included in a drainage master plan shall be master

planned by the Responsible Party as part of the annexation where practical.

(c)	Special Planning Areas

Presently, there are areas in the City where significant drainage problems currently

exist. Any new development or redevelopment in these areas may compound the existing

drainage problems.

The City requires analysis and/or definition of additional facilities required for

development and redevelopment in current drainage problem areas as defined by the

City. In addition to these areas, there are areas in the City where presently no

outlet exists for drainage by gravity to the Major Drainageway System.

(d)	Public Improvements

When the drainage master plans identify that public improvements are justified,

mechanisms for funding the improvements are required.

Included with the public improvements defined by drainage master plans is the

Local Drainage System and the Major Drainageway System. The Local Drainage System

consists of curb and gutter, inlets and storm sewers, culverts, bridges, swales,

ditches, channels, detention areas, and other drainage facilities within the

development required to convey the minor and major storm runoff to the Major

Drainageways. The Major Drainageway System consists of channels, storm sewers,

bridges, detention areas, and other facilities serving more than the subdivision

or property in question.

The City requires that all new development and redevelopment shall participate in

the drainage improvements as set forth below:

1.	Design and construct the local drainage system as defined by the Phase III

Drainage Report Plan (subsection 402.4-402.5 of these Standards and

Specifications.

2.	Design and construct connection of the local drainage system to the major

drainageway system.

3.	Equitable participation in the design and construction of the major drainageway

system within the development as defined by adopted master drainage plans

(subsection 403.3(b) of these Standards and Specifications) or as required by

the City and designated in the Phase III Drainage Report.

(e)	Floodplain Management

The City has adopted floodplain regulations as part of the City Code (Chapter 25,

Article 23).

(f)	Storm Runoff Detention and Water Quality Enhancement

The City requires on-site detention for all new development, expansion, and

redevelopment. The required minimum detention volume and maximum release rates

at these volumes for the 10-year and 100-year recurrence interval storm shall be

determined in accordance with the procedure and data set forth in these Standards

and Specifications.

The value of storm runoff detention as part of the urban system has been explored by

many individuals, agencies, and professional societies. Detention is considered a

viable method to reduce urban drainage costs. Temporarily detaining a few acre-feet

of runoff can significantly reduce downstream flood hazards as well as pipe and

channel requirements in urban areas. Storage also provides for sediment and debris

collection that helps improve the water quality of the runoff. Thus, public health

benefits may accrue from storage of storm runoff. However, all benefits can only

be obtained through consistent administration of the detention policy. This policy

may be adjusted by adopted master plans.

Exemptions from the detention requirement may be granted for in-fill areas and for

additions to existing buildings and paved areas, provided the total impervious

area of the in-fill or the total of all expansions cover less than 10,000 square

feet of impervious paved and roof surface. Exemptions shall also be considered for

rural development. On-site detention requirements shall be waived where regional

detention facilities are sized with the capacity to accommodate flows from a

fully developed basin and are publicly owned and maintained.

(g)	Operations and Maintenance

An important part of all storm drainage facilities is the continued maintenance of

facilities to ensure they shall function as designed. Maintenance of detention

facilities involves removal of debris and sediment. Such tasks are necessary to

preclude the facility from becoming unhealthy and to retain the effectiveness of

the detention basin. Sediment and debris must also be periodically removed from

channels and storm sewers. Trashracks and street inlets must be regularly cleared

of debris to maintain system capacity. Channel back erosion, damage to drop

structures, crushing of pipe inlets and outlets, and deterioration to the facilities

must be repaired to avoid reduced conveyance capability, unsightliness, and ultimate

failure.

Maintenance responsibility lies with the owner of the land, except as modified by

specific agreement. Maintenance responsibility shall be delineated on Final Plats

and Final Development Plans. Maintenance access for detention ponds need to be

specified but must be adequate for maintenance and be shown on the Final Plats and

Final Development Plans.

The City requires that maintenance access be provided to all storm drainage

facilities to assure continuous operational capability of the system. The property

owner shall be responsible for the maintenance of all privately owned drainage

facilities including inlets, pipes, culverts, channels, ditches, hydraulic

structures, and detention basins located on their land unless modified by the

Developer's Agreement. Should the property owner fail to adequately maintain said

facilities, the City shall have the right to enter said land for the purposes of

operations and maintenance. All such maintenance costs shall be assessed to the

property owner.

The easements required to provide adequate maintenance access are as follows:

TABLE 400-1

REQUIRED OPERATIONS & MAINTENANCE EASEMENT

DRAINAGE                                                     EASEMENT

FACILITY                                                      WIDTH

1.	Storm Sewer

(a) less than 36 inch dia.                              20'

(b) equal to or greater than 36 inch dia.               25'

Twice the pipe invert depth with

sewer placed within the middle

one-third of the easement

(minimum width = 20', maximum

width = 30')

2.	Open Channel/Swales

(a) Q less than 20 cfs	        15', including channel/swale and access road

(b) Q less than 100 cfs	        25', including channel/swale and access road

(c) Q greater than 100 cfs                 see Figures 400-8, 400-9 and 400-10

3.	Detention Pond	            As required to contain storage and

associated facilities plus adequate

maintenance access around perimeter.

1.0 freeboard - hw/d ratio of outlet pipe

In some instances within a subdivision, a property owner unknowingly blocks a

drainage path by installing fences, shrubs, or other obstructions along a side or

back lot line swale. The obstructions can block the free flow of drainage, resulting

in damage to upstream properties. All drainageways must be clearly defined and

maintained by providing easements or rights-of-way for storm runoff. Also, when

surface or subsurface drainage from public lands (i.e., streets) is allowed to flow

across adjacent private lands, such as a reverse draining cul-de-sac, damage to

private property can occur. To minimize these problems, the City shall require the

dedication of additional easements or rights-of-way.

The City requires dedicated drainage easements whenever surface or subsurface

drainage from public property drains across private property. A dedicated drainage

easement shall be provided in accordance with Table 400-1.

Drainage easements shall be shown on the final plats and any development plans and

state that the City has the right of access on the easements which shall be kept

clear of obstructions to the flow and/or obstructions to maintenance access.

(h)	Erosion and Sedimentation Control

The clearing and stripping of land for development can cause high localized erosion

rates with subsequent deposition and damage to off-site properties. Whereas erosion

and sedimentation is a natural process, the intensity is increased by development

which can destroy the aesthetic and practical values of other properties, streams,

lakes and downstream drainage facilities. The purpose of implementing an erosion

and sedimentation control plan is to reduce the process to an acceptable level

without placing undue burdens on the homeowner, builder, downstream drainageway or

community. The extent and detail of the plan may be a function of the site area.

The City requires an erosion and sedimentation plan be prepared and instituted for

all new development and any redevelopment in accordance with these Standards and

Specifications.

403.4	Technology Planning and Design

(a)	Drainage Criteria

The design criteria presented herein represents the state-of-the-art for stormwater

management. The criteria are intended to establish guidelines, standards, and

methods for effective planning and design. The criteria should be revised and

updated as necessary to reflect advances in the field of urban drainage engineering

and urban water resources management.

The City requires that all storm drainage facilities shall be planned and designed

in accordance with the criteria set forth in these Standards and Specifications.

The criteria shall be revised or amended as new technology is developed and/or

experience gained in the use of this document.

Due to the dynamic nature of urbanization, the needs of the public shall change

with time, requiring adjustment of design concepts. Therefore, a time limitation

on the approved construction plans shall be made.

Construction of any drainage facility not initiated within a six-month period from

time of development permit approval shall be re-evaluated and subject to approval

by the City.

(b)	Minor and Major Drainage System

Every urban area has two separate and distinct drainage systems, whether or not

they are actually planned or designed. One is the Minor Drainage System and the

other is the Major Drainage System, which are combined to form the Total Drainage

System.

The Minor Drainage System is designed to transport the runoff from five year

frequency events with a minimum disruption to the urban environment. Minor storm

drainage can be conveyed in the curb and gutter area of the street or roadside

ditch (subject to street classification and capacity, as defined herein), by

storm sewer, channel, or other conveyance facility.

All minor drainage systems shall be sized without accounting for peak flow

reductions from on-site detention.

The Major Drainage System is designed to convey runoff from the 100-year

recurrence interval flood to minimize health and life hazards, damage to

structures, and interruption to traffic and services. Major storm flows can be

carried in the urban street system (within acceptable depth criteria), channels,

storm sewers, and other facilities.

All subdivisions shall include the planning, designing, and implementation for both

the minor and major drainage systems in accordance with the following recurrence

intervals:

TABLE 400-2

RECURRENCE INTERVAL (YEARS)

MINOR DRAINAGE               MAJOR DRAINAGE

LAND USE               SYSTEM                       SYSTEM

Residential-Urban         5                           100

Residential-Rural         5                           100

Commercial-Business       5                           100

Industrial                5                           100

Open Space                5                           100

School                    5                           100

(c)	Storm Runoff

The UD&FCD Manual allows storm runoff to be determined by the CUHP Manual for

basins greater than 90 acres (except as noted herein) and by the Rational Method

for basins less than 160 acres (Urban Drainage say 90). (Between 90 acres and 160

acres it is optional as to which method to use).

The City allows storm runoff to be determined by either the rational method or the

Nebraska Urban Hydrograph Procedure (NUHP), within the limitations as set forth in

this criteria. For basins larger than 160 acres, the peak flows and volumes shall

be determined by the Nebraska Urban Hydrograph Procedure.

(d)	Streets

Streets are an integral part of the urban drainage system and may be used for

transporting storm runoff up to design limits. The engineer designer should

recognize that the primary purpose of streets is for traffic, and therefore the

use of streets for storm runoff must be restricted. The City allows the use of

streets for drainage within the following limitations:

TABLE 400-3

ALLOWABLE USE OF STREETS FOR MINOR STORM RUNOFF

DRAINAGE             MAXIMUM THEORETICAL

CLASSIFICATION       STREET ENCROACHMENT

Type A               No curb overtopping. Flow may be spread to crown of

(Local service,      street. (Flow may spread to back of the sidewalk

Local Collector)     for a 4-inch combination curb and sidewalk).

Type B               No curb overtopping. Flow spread must leave at least

(Collectors)         one 10-foot lane free of water, 5-feet either side of the

street crown.

Type C               No curb overtopping. Flow spread must leave at least

(Arterials)          two 10-foot lanes free of water, 10-feet each side of the

street crown or median.

The maximum allowable street flow shall be the product of the flow calculated at

the "Maximum Theoretical Street Encroachment" and the required reduction factor

as provided in these criteria.

TABLE 400-4

ALLOWABLE USE OF STREETS FOR MAJOR STORM RUNOFF

DRAINAGE                MAXIMUM THEORETICAL

CLASSIFICATION          DEPTH

Type A and B            The depth of water at the gutter shall not

(All Local and          exceed 12-inches.

and Collectors)

Type C                  To allow for emergency vehicles, the depth of water

(Arterials)             shall not exceed 6-inches at the street crown and 12-inches

at the gutter flowline, whichever is more restrictive.

The maximum allowable street flow shall be the product of the flow calculated at the

"Maximum Theoretical Depth" and the required reduction factor as provided in these

criteria.

TABLE 400-5

ALLOWABLE CROSS STREET FLOW

MINOR DRAINAGE         MAJOR DRAINAGE

DRAINAGE              SYSTEM MAXIMUM         SYSTEM MAXIMUM

CLASSIFICATION        DEPTH                  DEPTH

Type A                6-inches of depth      12-inches of depth at

(Local Service,       in cross pan or        gutter flowline

(Local Collector)     gutter flowline

Type B                6-inches of depth      12-inches of depth at

(Collector)           at the gutter          gutter flowline

flowline

Type C                Zero                   Zero

(Arterials)

Cross street flow can occur in an urban drainage system under three conditions. One

condition occurs when the runoff in a gutter spreads across the street crown to the

opposite gutter. The second is when cross pans are used. The third condition occurs

when the flow in a drainageway exceeds capacity (for the appropriate design storm)

of a road culvert and subsequently overtops the crown of the street.

TABLE 400-6

ALLOWABLE CULVERT OVERTOPPING

MINOR DRAINAGE        MAJOR DRAINAGE

DRAINAGE              SYSTEM MAXIMUM        SYSTEM MAXIMUM

CLASSIFICATION        DEPTH                 DEPTH

Types A and B         None                  12-inches of depth at the flowline

(All Local and

(Collectors)

Type C                None                  None

(Arterials)                                 The minimum clearance between the low

chord or culvert crown and the energy

grade line shall be six-inches for

basins less than two square miles, one

foot for basins up to 10 square miles,

and two feet for basins greater than 10

square miles.

The maximum headwater for the 100-year design flows shall be one and one-half times the

culvert diameter or one and one-half times the rise dimension for pipe shapes other than

round. (Type A and Type B streets only.)

(e)	Floodproofing

Floodproofing can be defined as those measures that reduce the potential for flood

damages to existing properties within a floodplain. The floodproofing measures can

range from elevating structures to intentional flooding of non-critical building

spaces to minimize structural damages. Floodproofing measures are only a small part

of good floodplain management that encourages wise floodplain development to

minimize the adverse effects of floods.

Floodproofing of existing structures not in conformance to the adopted floodplain

regulations shall be accomplished by utilizing the criteria presented in the

"Nebraska Floodproofing Manual" prepared by The Department of Natural Resources,

Nebraska Water Conservation Board, dated ????????????????????.

403.5	Irrigation Facilities

(a)	Drainageway Interaction

There are many irrigation ditches and reservoirs in the City area. The ditches and

reservoirs have historically intercepted the storm runoff from the rural and

agricultural type basins, generally without major problems. With urbanization of the

basins, however, the storm runoff has increased in rate, quantity and frequency, as

well as changes in water quality. The irrigation facilities can no longer be

utilized indiscriminately as drainage facilities and therefore, policies have been

established to achieve compatibility between urbanization and the irrigation

facilities.

In evaluating the interaction of irrigation ditches with a major drainageway for the

purpose of basin delineation, the ditch should not be used as a basin boundary.

The drainage analysis shall assume that an irrigation ditch does not intercept the

storm runoff from the upper basin and that the upper basin is tributary to the basin

area downstream of the ditch.

(b)	Storage Facilities

The problem of dam safety and the related hazard of the emergency spillways has been

brought to the attention of the public by recent nationwide dam failures, and is the

subject of a National Dam Safety Program by the Federal government. Jurisdictional

dams are classified by the State Engineer as either low, moderate, or high hazard

structures depending on conditions downstream. Dams are classified as high hazard

structures when, in the event of failure, there is potential loss of life. Dams

presently rated as low or moderate hazard structures may be changed to high hazard

rating if development occurs within the potential path of flooding due to a dam

breach. In this case, the reservoir Responsible Parties would be liable for the

cost of upgrading the structures to meet the higher hazard classification. Even

though someone other than the dam Responsible Party builds in that area.

Pursuant to Section 37-87-123, CRS, as amended, the Office of the State Engineer

has prepared flood hazard maps resulting from the failure of the high hazard dams

within the state. These reports have been made available to various cities, towns,

and counties that may be affected by a dam breach.

For hydrologic purposes, all private dams shall be ignored in determination

definition of floodplains.

(c)	Irrigation Ditches

Irrigation ditches are designed with flat slopes and limited carrying capacity,

which decreases in the downstream direction. As a general rule, irrigation ditches

cannot be used as an outfall point for the storm drainage system because of these

physical limitations. In addition, certain ditches are abandoned after urbanization

and, therefore, could not be successfully used for storm drainage.

404	RAINFALL

404.1	Introduction

Presented in this section is the design rainfall data to be used with the Colorado Urban

Hydrograph Procedure (CUHP) and the Rational Method. All hydrological analysis within

the jurisdiction of the criteria shall use the rainfall data presented for calculating

storm runoff.

The design storms and time intensity frequency curves for the City were developed using

the rainfall data and procedures presented in the UD&FCD Manual and are presented herein

for convenience.

404.2	CUHP Design Storms

For drainage basins less than five square miles, a two-hour storm distribution without

area adjustment of the point rainfall values shall be used for CUHP.

For drainage basins between five and ten square miles, a two-hour storm distribution is

used but the incremental rainfall values are adjusted for the large basin area in

accordance with suggested procedures in the NOAA Atlas for Colorado. The adjustment is

an attempt to relate the average of all point values for a given duration and frequency

within a basin to the average depth over the basin for the same duration and frequency.

For drainage basins between ten and twenty square miles, a three-hour storm duration with

adjustment for area shall be used. The distribution for the last hour was obtained by

uniformly distributing the difference between the two- and three-hour point rainfall

values. The adjustment for area was obtained from the NOAA Atlas for Colorado. The

incremental rainfall distribution for all basin areas up to 20 square miles is presented

in Figure 400-49.

404.3	Time-Intensity-Frequency Curves

The one-hour design point rainfall values obtained from the NOAA Atlas for Colorado area

as follows:

ONE-HOUR POINT RAINFALL (IN.)

2-YEAR      5-YEAR      10-YEAR      50-YEAR      100-YEAR

1.00        1.42         1.68         2.35          2.71

The Time-Intensity-Frequency curves were developed by distributing the one-hour point

rainfall values using the factors obtained from the NOAA Atlas presented below:

FACTORS FOR DURATIONS OF LESS THAN ONE HOUR

Duration (minutes)        5          10          15          30

Ratio to 1-hour depth     0.29       0.45        0.57        0.79

Source: NOAA Atlas 2, Volume III, Colorado latest edition

The point values were then converted to intensities and plotted on Figure 400-50. The

data are also presented in Figure 400-51.

405	RUNOFF

405.1	Introduction

This subsection presents the criteria and methodology for determining the storm runoff

design peaks and volumes to be used in the City in the presentation of storm drainage

studies, plans, and facility design. The details of the rainfall/runoff models are

presented in the UD&FCD Manual. The specific input data requirements and modifications

to the procedures are presented in this subsection.

405.2	Rational Method

The Rational Method, in widespread use in the Denver Region, shall continue to be

utilized for the sizing of storm sewers and for determining runoff magnitude from

unsewered areas. The new limit of application of the Rational Method is approximately

160 acres. It has been concluded that, for tributary basins in excess of 160 acres, the

cost of drainage works justifies significantly more study, thought, and judgement on

the part of the engineer than is permitted by the Rational Method. When the urban

drainage basin exceeds 160 acres, the CUHP method represents better practice and should

be used.

The procedure for the Rational Method, as explained in the manual, Volume-1 "Runoff"

(Revised May 1, 1984), shall be followed in the preparation of drainage reports and

storm drainage facility designs in the City.

Standard forms for the calculation of Time of Concentration and Storm Drainage System

Design have been provided at the end of these criteria.

405.3	Colorado Urban Hydrograph Procedure

The Colorado Urban Hydrograph Procedure (CUHP) was originally developed for the Denver

area at the time the manual was prepared. The method is generally applicable to basins

greater than 90 acres (see subsection 405.9). However, the CUHP is required for

watershed areas larger than 160 acres. The procedures for the CUHP, as explained in the

manual, Volume-1 "Runoff," shall be followed in the preparation of drainage reports and

storm drainage facility designs in the City. The design storms to be used with the CUHP

method are presented in Table 410.

405.4	Storm Flow Analysis

When determining the design storm flows, the engineer shall follow particular criteria

and guidelines to assure that minimum design standards and uniformity of drainage

solutions are maintained throughout the City. The information presented herein shall be

used by the design engineer in the development of design storm runoff.

405.5	On-Site Flow Analysis

When analyzing the flood peaks and volumes, the design engineer shall use the proposed

fully developed land use plan to determine runoff coefficients. In addition, the

engineer shall take into consideration the changes in flow patterns (from the undeveloped

site conditions) caused by the proposed street alignments. When evaluating surface flow

times, the proposed lot grading shall be used to calculate the time of concentration or

the CUHP parameters.

405.6	Off-Site Flow Analysis

The analysis of off-site runoff is dependent on the development status and whether the

tributary off-site area lies within a major drainageway basin as defined in subsection

403.2(e). In all cases, the minor system is designed for the fully developed minor

storm runoff (subsection 403.4(b)) with the benefits of on-site detention. In some

cases credit is given for detention for the design of the major system.

405.7	Tributary Area Within a Major Drainageway Basin

(a)	Where the off-site area is undeveloped, the runoff shall be calculated assuming the

basin is fully developed as defined by the Planning Department. If this information

is not available, then the runoff shall be calculated using the coefficients

defined in Table 3-1 of Section 3.6, "Runoff," Volume I of the UD&FCD Manual,

"Undeveloped Areas - Off-site Flow Analysis." Credit shall be given for on-site

detention in the off-site area for any design frequency.

(b)	Where the off-site area is fully or partially developed, the storm runoff shall be

based upon the existing platted land uses and topographic features. Credit may be

given for on-site detention in the off-site area for any design frequency.

405.8	Tributary Area Not Within a Major Drainageway Basin

(a)	Where the off-site area is undeveloped, the minor system runoff shall be calculated

assuming the basin is in its existing condition. If this information is not

available, then the runoff shall be calculated as stated in Section 405.7, without

credit for on-site detention in the off-site area.

The major system runoff (i.e., 10-year and 100-year) may be calculated assuming the

historic runoff rates computed in accordance with procedures described in these

criteria.

(b)	Where the off-site area is fully or partially developed, the storm runoff shall be

based on the existing platted land uses and topographic features, unless on-site

detention in the off-site area has been constructed and accepted by the City.

However, credit may be given for on-site detention in the off-site area for the

minor system design.

405.9	CUHP Computer Program

A computer program has been developed to calculate hydrographs using the CUHP method.

This program is available for use on both large mainframe computers and on the smaller

IBM-PC XT or IBM-PC AT personal computers. In addition, the personal computer version

has an added capability of using CUHP to compute runoff hydrographs for basins of 10-

acres or larger in size. Only with the personal computer version with 10- to 90-acre

CUHP basins shall be allowed. Specific details of the required input for this version

are available in the CUHPE/PC Version Users Manual. Both the CUHPD (large mainframe)

and CUHPE/PC (personal computer) compute programs can be obtained by contacting the

UD&FCD at 2480 West 26th Avenue, Suite 156-B, Denver, Colorado 80211.

406	OPEN CHANNELS

406.1	Introduction

This chapter addresses the technical criteria for the hydraulic evaluation and hydraulic

design of open channels in the City. The information presented herein is considered to

be a minimum standard. In many instances, special design or evaluation techniques shall

be required. Except as modified herein, all open channel criteria shall be in accordance

with the UD&FCD Manual.

406.2	Channel Types

The channels in the City area are defined as natural or artificial. Natural channels

include all water courses that have occurred naturally by the erosion process such as

??????????????????????. Artificial channels are those constructed or developed by

human effort such as ??????????????????, large designated floodways, irrigation canals

and flumes, roadside ditches, and grassed channels.

(a)	Natural Channels

The hydraulic properties of natural channels vary along the channel reach and can

be either controlled to the extent desired or altered to meet given requirements.

The initial decision to be made regarding natural channels is whether or not the

channel is to be protected from erosion due to high velocity flows, or protected

from excessive silt deposition due to low velocities.

Many natural channels in urbanized and to-be-urbanized areas have mild slopes, are

reasonably stable, and are not in a state of serious degradation or aggradation.

However, if a natural channel is to be used for carrying storm runoff from an

urbanized area, the altered nature of the runoff peaks and volumes from urban

development shall cause erosion. Detailed hydraulic analysis shall be required for

natural channels in order to identify the erosion tendencies. Some on-site

modifications of the natural channel may be required to assure a stabilized

condition.

The investigations necessary to assure that the natural channels shall be adequate

are different for every waterway. The engineer designer must prepare cross sections

of the channel, define the water surface profile for the minor and major design

flood, investigate the bed and bank material to determine erosion tendencies, and

study the bank slope stability of the channel under future conditions of flow.

Supercritical flow does not normally occur in natural channels, but calculations

must be made to assure that the results do not reflect supercritical flow.

(b)	Grass Lined Channels

Grass lined channels are the most desirable of the artificial channels. The grass

shall stabilize the body of the channel, consolidate the soil mass of the bed,

check the erosion on the channel surface, and control the movement of soil particles

along the channel bottom. The channel storage, the lower velocities, and the green

belt multiple-use benefits obtained create significant advantages over other

artificial channels.

The presence of grass in channels creates turbulence which results in loss of energy

and increased flow retardance. Therefore, the designer must give full consideration

to sediment deposition and to scour, as well as hydraulics. Unless existing

development within the City restricts the availability of right-of-way (ROW), only

channels lined with grass shall be considered acceptable for major drainageways.

(Retardance C should be considered for undeveloped channels for velocity

consideration.)

For the purpose of these criteria, sandy soils are defined as non-cohesive sands

classified as SW, SP, or SM in accordance with the Unified Soil Classification

System.

(c)	Concrete Lined Channels

Concrete lined channels for major drainageways shall be permitted only where

ROW restrictions within existing development prohibit grass lined channels. The

lining must be designed to withstand the various forces and actions which tend

to overtop the bank, deteriorate the lining, erode the soil beneath the lining,

and erode unlined areas, especially for the supercritical flow conditions.

If the project constraints suggest the use of a concrete channel for a major

drainageway, the applicant shall present justification and design to the City

Engineer for consideration.

A Design Report is required for approval of a concrete lined channel. The contents

of such report shall be determined by the City Engineer. On the Record Drawings,

the engineer shall be required to certify that the concrete used in the lining was

tested and meets the accepted specifications.

(d)	Rock Lined Channels

Riprap lined channels are generally discouraged and shall be permitted only in

areas of existing development where ROW for major drainageways is limited and

such limitation prohibits the use of grass lined channels. The advantage of rock

lining a channel is that a steeper channel grade can be used due to the higher

friction of the rock. Also, steeper side slopes are permitted. Rock linings

(i.e., revetments) are permitted as a means of controlling erosion for natural

channels. The disadvantages are the large initial cost of construction and the

high maintenance costs due to vandalism and other factors.

If the project constraints suggest the use of riprap lining for a major drainageway,

then the engineer must present the concept, with justification, to the City Engineer

for consideration of a waiver from these criteria. The design of rock lined channels

shall be in accordance with the UD&FCD Manual, Volume 2, "Major Drainage Section 5 -

Riprap," current revision.

(e)	Wetlands Vegetation Bottom Channels

The choice for a channel that a designer has are many, depending upon hydraulic

practice, environmental design, sociological impact, and basic project requirements.

However, prior to choosing the channel type, the need or desire for channelization

should be established. Once a decision is made to channelize, then investigations

into the status of the present drainageway are necessary to define the constraints

on the channel design. For instance, if the channel presently has wetland

characteristics, then the Section 404 requirements of the Clean Water Act may

require that the design include wetlands. The designer should contact the Corps of

Engineers for additional information.

The process of choosing a channel configuration and the design criteria for a

wetlands bottom channel (if this type is selected) has been developed by the UD&FCD

latest revision, 1991. The designer is referred to these interim criteria (Section 2

of the UD&FCD Manual under Major Drainage) for the procedures and criteria for all

channel design.

(f)	Other Lining Types

The use of synthetic fabrics in construction and geotechnical engineering has

increased tremendously in the last decade or more. The use of fabrics for drainage

construction (i.e., erosion control liners) has actually taken place over the past

several years. The placement of a slope revetment mat is a method of erosion

control and the subject of discussion in this section.

The mattresses generally consist of double layers of woven fabric forms placed on

the slope to be protected, and filled with concrete or grout. This type of forming

system is a simple, fast, and economical technique for the placement of concrete

for slope protection both above and below the water without the need for dewatering.

The performance characteristics and cost advantages make the process adaptable for

stabilizing and protecting shorelines, leaves, dikes, canals, holding basins, and

similar erosion control projects.

The systems make use of the pressure injection of fluid fine-aggregate concrete

into flexible fabric forms. Controlled bleeding of mixing water through the porous

fabric produces all the desirable features of low water/cement ratio mortar--rapid

stiffening, high strength, and exceptional durability.

For normal installations, the fabric forms, prefabricated to job specifications and

dimensions, are simply spread over the terrain, which has received minimal grading.

The fabric form is then pumped full of mortar. This same concept can be used where

slide problems are caused by eroding of the toe of the slopes, and where access is

difficult for placement riprap. See Figure 400-47 for typical sections of

mattresses.

There are several manufacturers of synthetic fabrics for erosion protection.

Included in this category of channel lining are the products which consist of

discrete blocks on a continuous fabric backing.

The use of synthetic fabrics for lining of channels for major drainageways is

restricted to areas of existing development where the ROW constraints prohibit

the use of a grass lined section. Such use shall be allowed only upon written

approval by the City Engineer. The linings shall be restricted to channels with a

Froude number of 0.8 or less.

406.3	Flow Computation

Uniform flow and critical flow computations shall be in accordance with the UD&FCD

Manual, Section 2.2.3 and 2.2.4, "Major Drainage," and shall use the Manning's equation

as follows:

Q =  1.49 (AR2/3 S1/2)           (Equation 400-1)

n

where   Q = flow rate (cfs)

n = Manning's roughness coefficient

A = area (ft)

R = hydraulic radius

S = energy grade-line slope (ft/ft)

406.4	Design Standards for Major Drainageways

These standards cover the design of major drainageways as defined by subsection 403.2(e).

The design standards for open channels cannot be presented in a step-by-step fashion

because of the wide range of design options available to the design engineer. Certain

planning and conceptual design criteria are particularly useful in the preliminary design

of a channel. These criteria, which have the greatest effect on the performance and cost

of the channel, are discussed below.

(a)	Natural Channels

The design criteria and evaluation techniques for natural channels are:

1.	The channel and overbank areas shall have adequate capacity for the 100-year

storm runoff.

2.	Natural channel segments which have a calculated Froude number greater than

0.95 for the 100-year flood peak shall be protected from erosion.

3.	The water surface profiles shall be defined so that the floodplain can be

zoned and protected.

4.	Filling of the Flood Control Overlay District (i.e., the floodplain area,

see Appendix for Floodplain Regulations) reduces valuable channel storage

capacity and tends to increase downstream runoff peaks.

5.	Roughness factors (n), which are representative of unmaintained channel

conditions, shall be used for the analysis of water surfaced profiles.

6.	Roughness factors (n), which are representative of maintained channel

conditions, shall be used to determine velocity limitations.

7.	Erosion control structures, such as check drops or check dams, may be

required to control flow velocities, including the minor storm runoff.

8.	Plan and profile drawings of the floodplain shall be prepared. Appropriate

allowances for known future bridges or culverts, which can raise the water

surface profile and cause the floodplain to be extended, shall be included in

the analysis. The applicant shall contact the City Engineer for information on

future bridges and culverts.

With most natural waterways, erosion control structures should be constructed at

regular intervals to decrease the thalweg slope and to control erosion. However,

these channels should be left in as near a natural condition as possible. For that

reason, extensive modifications should not be undertaken unless they are found to

be necessary to avoid erosion with subsequent deposition downstream.

The usual rules of freeboard depth, curvature, and other rules that are applicable

to artificial channels, do not apply for natural channels. All structures

constructed along the channel shall be elevated a minimum of one foot above the

100-year water surface. There are significant advantages that may occur if the

designer incorporates into his planning the overtopping of the channel and localized

flooding of adjacent areas which are laid out and developed for the purpose of being

inundated during the major runoff peak.

If a natural channel is to be utilized as a major drainageway for a development,

then the applicant shall meet with the City Engineer to discuss the concept and to

obtain the requirements for planning and design documentation. Approval of the

concept and design shall be made in accordance with the requirements of subsection

402 of these Standards and Specifications.

(b)	Grass Lined Channels

Key parameters in grass lined channel design include velocity, slopes, roughness

coefficients, depth, freeboard, curvature, cross section shape, and lining

materials. Other factors such as water surface profile computation, erosion

control, drop structures, and transitions also play an important role. A

discussion of these parameters is presented below.

1.	Flow Velocity

The maximum normal depth velocity for the 100-year flood peak shall not exceed

7.0 feet per second for grass lined channels, except in sandy soil where the

maximum velocity shall not exceed 5.0 feet per second. The Froude number

(turbulence factor) shall be less than 0.8 for grass lined channels. Grass

lined channels having a Froude number greater than 0.8 shall not be permitted.

The minimum velocity, wherever possible, shall be greater than 2.0 feet per

second for the minor storm runoff.

2.	Longitudinal Channel Slopes

Grass lined channel slopes are dictated by velocity and Froude number

requirements. Where the natural topography is steeper than desirable, drop

structures shall be utilized to maintain design velocities and Froude numbers.

3.	Freeboard

Except where localized overflow in certain areas is desirable for additional

ponding benefits of other reasons, the freeboard for the 100-year flow shall

be as follows. The minimum freeboard shall be 1.0 foot.

Hfb = 0.5 =  V2              (Equation 400-2)

2g

Where   Hfb     = freeboard height (feet)

V       = average channel velocity (feet per second)

g       = acceleration of gravity = 32.2 ft/sec2

4.	Curvature (Horizontal)

The center line curvature shall have a radius twice the the top width of the

design flow but not less than 100 feet.

5.	Roughness Coefficient

The variation of Manning's "n" with the retardance and the product of mean

velocity and hydraulic radius, as presented in Figure 400-7 shall be used in

the capacity computation.

Retardance curve C shall be used to determine the channel capacity, since a

mature channel (i.e., substantial vegetation with minimal pervious maintenance)

shall have a higher Manning's "n" value. However, a recently constructed

channel shall have minimal vegetation and the retardance shall be less than the

mature channel. Therefore, retardance curve D (see Figure 400-7) shall be used

to determine the limiting velocity in a channel.

6.	Cross Sections

The channel shape may be almost any type suitable to the location and to the

environmental conditions. Often the shape can be chosen to suit open space

and recreational needs. Figure 400-8 and 400-9 present two cross sections for

use with non-sandy soils. Figure 400-10 is the required cross section for

sandy soils. The limitations within which the design must fall for the major

storm design flow include:

a.  Trickle Channel

The base flow shall be carried in a trickle channel except for sandy

soil. The minimum capacity shall be 1.0 percent to 3.0 percent of the

100-year flow but not less than 1 cfs. Trickle channels shall be

constructed of concrete or other approved materials to minimize erosion,

to facilitate maintenance, and to aesthetically blend with the adjacent

vegetation and soils. Recommended trickle channel sections are presented

in Figure 400-12. The minimum trickle channel width shall be four feet.

b.  Low Flow Channel

A main channel is required for sandy soils as shown in Figure 400-10. The

side slopes may be from 2:1 to 2.5:1 and shall be riprap lined. The depth

of the main channel is not included in the normal depth limitations. A

main channel can also be used for non-sandy soils, subject to the

conditions shown in Figure 400-8 and 400-9.

c.  Bottom Width

The minimum bottom width shall be consistent with the maximum depth and

velocity criteria. The minimum bottom width shall be four feet or the

trickle channel width when trickle channel is required.

d.  Easement/Right-of-Way Width

The minimum easement/ROW width shall include freeboard and a 12-foot wide

maintenance access road.

e.  Flow Depth

The maximum design depth of flow (outside the trickle channel area and main

channel area for sandy soils) for the 100-year flood peak shall be limited

to five feet in grass lined channels.

f.  Maintenance Access Road

A maintenance access road shall be provided along the entire length of all

major drainageways with a minimum passage width of 12 feet. The City may

require the road to be surfaced with six inches of Class 2 road base or

concrete slab. (Refer to Section 403.3(g) of these criteria.)

g.  Side Slopes

Side slopes shall be four (horizontal) to one (vertical) or flatter.

7.	Grass Lining

The grass lining for channels shall be in accordance with the UD&FCD Manual,

Section 2.3.2, "Major Drainage - Grass Lined Channels -Grass"; "Guidelines for

Development and Maintenance of Natural Vegetation," and as required by the

City.

8.	Erosion Control

The requirements for erosion control for grass lined channels shall be as

defined in the UD&FCD Manual, Section 2.3.6, "Major Drainage Erosion Control."

The design of riprap and erosion control devices shall be in accordance with

Section 411.1 and 411.2 of these Standards and Specifications.

9.	Water Surface Profiles

Computation of the water surface profile shall be presented for all open

channels utilizing standard backwater methods, taking into consideration

losses due to changes in velocity of channel cross section, drops, waterway

openings, or obstructions. The energy gradient shall be shown on all

preliminary drawings.

(c)	Concrete Lined Channels

The criteria for the design and construction of concrete lined channels is presented

below:

1.	Hydraulics

a.  Freeboard

Adequate channel freeboard above the designed water surface shall be

provided and shall not be less than that determined by the following:

Hfb = 2.0 + 0.025 V (d)1/3     (Equation 400-3)

where    Hfb = freeboard height (feet)

V = velocity (feet per second)

d = depth of flow (feet)

Freeboard shall be in addition to superelevation, standing waves, and/or

other water surface disturbances. These special situations are to be

addressed in a Design Report to be submitted with the construction drawings

and specifications (subsection 402.5). Concrete side slopes shall be

extended to provide freeboard.

b.  Superelevation

Superelevation of the water surface shall be determined at all horizontal

curves, and design of the channel section adjusted accordingly.

c.  Velocities

Flow velocities shall not exceed 18 fps during the 100-year flood.

2.	Concrete Materials

The minimum concrete material specifications are as follows:

a.  Cement type: sulphate resistant (Type V).

b.  Minimum cement content: 550 lbs/C.Y.

c.  Maximum water-cement ratio: 0.50 (Six gals. per sack).

d.  Maximum aggregate size: 1 1/2 inches.

e.  Air entrainment content: four to seven percent.

f.  Slump: two to four inches.

g.  Minimum compressive strength (f'c): 3750 psi at 28 days.

h.  Admixtures: All proposed admixtures shall be discussed on the Design

Report and are subject to the City Engineer's approval.

3.	Concrete Lining Section

a.  All concrete lining shall have a minimum thickness of seven inches.

b.  The side slopes shall be a maximum of two (vertical) to one (horizontal),

or a structurally reinforced wall if steeper.

4.	Concrete Joints

a.  Channels shall be continuously reinforced with (without in previous report)

transverse joints. Expansion/contraction joints shall be installed where

new concrete lining is connected to a rigid structure or to existing

concrete lining that is not continuously reinforced.

b.  Longitudinal joints, where required, shall be constructed on the side walls

at least one foot vertically above channel invert.

c.  All joints shall be designed to prevent differential movement.

d.  Construction joints are required for all cold joints and where the lining

thickness changes. Reinforcement shall be continuous through the joint.

5.	Concrete Finish

The surface of the concrete lining shall be provided with a wood float finish.

Excessive working or wetting of the finish shall be avoided.

6.	Concrete Curing

All concrete shall be cured by the application of a liquid membrane forming

curing compound (white pigmented) upon completion of the concrete finish.

7.	Reinforcement Steel

a.  Steel reinforcement shall be minimum grade-40 deformed bars. Fabric mesh

may also be approved. Wire mesh shall not be used.

b.  Ratio of longitudinal steel area to concrete cross sectional area shall

be greater than .005.

c.  Ratio of transverse steel area to concrete cross sectional area shall be

greater than .0025.

d.  Reinforcing steel shall be placed at the center of the section with a

minimum clear cover of three inches adjacent to the earth.

e.  Additional steel as needed if a retaining wall structure is used.

8.	Earthwork

The following area shall be compacted to at least 95 percent of maximum

density as determined by ASTM D698 (Standard Proctor):

a.  The 12 inches of subgrade immediately beneath concrete lining (both

channel bottom and side slopes).

b.  Top 12 inches of maintenance road.

c.  Top 12 inches of earth surface within 10 feet of concrete channel lip.

d.  All fill material.

9.	Bedding

Provide six inches of granular bedding equivalent in gradation to 3/4 inch

concrete aggregate (Standard Specifications for Road & Bridge Construction,

CDOT, latest revision) under channel bottom and side slopes.

10.	Underdrain

Longitudinal underdrains shall be provided on 10-foot centers and shall

daylight at the check drops. A check valve or flap gate shall be provided at

the outlet to prevent backflow into the drain. Weep holes shall be provided

in vertical wall sections of the channel.

11.	Safety Requirements

a.  A six-foot high vinyl coated chain link, a comparable fence, or an

architecturally approved restraining device shall be installed to

prevent access wherever the 100-year channel flow depths exceed

three feet. Gates, with top latch, shall be placed at 250' intervals

and staggered where fence is required on both sides of the channel.

b.  Ladder-type steps shall be installed not more than 400 feet apart on

alternating side of the channel for channel depths in excess of three

feet. Bottom rung shall be placed approximately 12 inches vertically

above channel invert.

12.	Maintenance Access Road

A maintenance access road shall be provided along the entire length of all

major drainageways with a minimum passage width of 12 feet. The City may

require the road to be surfaced with six inches of Class 2 roadbase or

concrete slab (refer to Section 403.3(g) of these criteria).

(d)	Riprap Lined Channels

The criteria for the design and construction of riprap lined channels shall be in

accordance with the UD&FCD Manual, Volume 2, "Major Drainage - Riprap." Riprap

lined channels shall be designed a turbulence factor (Froude number) less than 0.8

for the 100-year flood peaks. The riprap shall be designed and constructed in

accordance with Section 411.2 "Hydraulic Structures - Riprap" of these criteria.

Freeboard and maintenance access road requirements shall be in accordance with the

standards for grass lined channels defined in Section 406.4(b) of these criteria.

(e)	Other Lining Types

The criteria for the design of major drainageway channels with linings other than

grass, rock, or concrete shall be dependent on the manufacturer's recommendations

for the specific product. The applicant shall be required to submit the technical

data in support of the proposed material. Additional information or calculations

may be requested by the City Engineer to verify assumptions or design criteria.

The following minimum criteria also shall apply.

1.	Flow Velocity

The maximum normal depth velocity shall be dependent on the construction

material used; however, the Froude number shall be less than 0.8.

2.	Freeboard

Defined by Equation 400-2.

3.	Curvature

The center line curvature shall have a minimum radius twice the top width

of the design flow but not less than 100 feet.

4.	Roughness Coefficient

A Manning's "n" value range shall be established by the manufacturer's date,

with the high value used to determine depth/capacity requirements and the

low value used to determine Froude number and velocity restrictions.

5.	Cross Sections

Same as for grass lined channels, subsection 406.4(b).

406.5	Design Standards for Small Drainageways

These standards cover the design of channels that are not classified as a major

drainageway in accordance with the policy of subsection 403.2(e). Additional flexibility

and less stringent standards are allowed for small drainageways.

(a)	Natural Channels (Small Drainageways)

The design criteria and evaluation techniques for natural channels are:

1.	The channel and overbank areas shall have adequate capacity of the 100-year

storm runoff.

2.	Natural channel segments that have a calculated Froude number greater than

0.95 for the 100-year flood peak shall be protected from erosion.

3.	Roughness factors (n), which are representative of unmaintained channel

conditions, shall be used for the analysis of water surface profiles.

4.	Roughness factors (n), which are representative of maintained channel

conditions, shall be used to determine velocity limitations.

5.	Erosion control structures, such as check drops or check dams, may be required

to control flow velocities, including the minor storm runoff.

6.	Plan and profile drawings shall be prepared showing the 100-year water surface

profile, floodplain, and details of erosion protection, if required.

(b)	Grass Lined Channels (Small Drainageways)

Key parameters in grass lined channel design include velocity, slopes, roughness

coefficients, depth, freeboard, curvature, cross section shape, and lining

materials. Other factors such as water surface profile computation, erosion control,

drop structures, and transitions also play an important role. A discussion of these

parameters is presented below.

1.	Flow Velocity

The maximum normal depth velocity of the 100-year flood peak shall not exceed

7.0 feet per second for grass lined channels, except in sandy soil where the

maximum velocity shall not exceed 5.0 feet per second (see section 406.2(b)).

The Froude number (turbulence factor) shall be less than 0.8 for grass lined

channels. Grass lined channels having a Froude number greater than 0.8 shall

not be permitted. The minimum velocity, wherever possible, shall be greater

than 2.0 feet per second for the minor storm runoff.

2.	Longitudinal Channel Slopes

Grass lined channel slopes are dictated by velocity and Froude number

requirements. Where the natural topography is steeper than desirable, drop

structures shall be used to maintain design velocities and Froude numbers.

3.	Freeboard

A minimum freeboard of one foot shall be included in the design for the 100-

year flow. For swales (i.e., small drainageways with a 100-year flow less than

20 cfs), the minimum freeboard requirements are 6 inches.

4.	Curvature (Horizontal)

The center line curvature shall have a minimum radius twice the top width of

the design flow but not less 50 feet. The minimum radius for channels with a

100-year runoff of 20 cfs or less shall be 25 feet.

5.	Roughness Coefficient

The variation of Manning's "n" with the retardance (curve "C") and the product

of mean velocity and hydraulic radius, as presented in Figure 400-7, shall be

used in the computation of capacity and velocity.

6.	Cross Sections

The channel shape may be almost any type suitable to the location and to the

environmental conditions. Some suggested cross sections are shown on Figures

400-8, 400-9, and 400-10. The section also may be simple V-Section for

swales (i.e. Q100 less than 20 cfs). The limitations on the cross section are

as follows:

a.  Trickle Channel

The base flow (except for swales) shall be carried in a trickle channel for

non-sandy soils. The minimum capacity shall be from 1.0 percent to 3.0

percent of the 100-year flow but not less than 1 cfs. The trickle channel

can be constructed of concrete, rock, cobbles, or other suitable materials.

For sandy soils, a main channel is required in accordance with section

406.4(b).

Factors to be considered when establishing the need for trickle channels

are: drainageway slope, soil type, and upstream impervious area. For 100

year runoff peaks of 20 cfs or less, trickle channel requirements shall

be evaluated for each case. Trickle channels help preserve swales crossing

residential property.

b.  Easement/Rights-of-Way Width

The minimum easement/ROW width shall include freeboard and should include

a 12-foot wide maintenance access road.

c.  Flow Depth

The maximum design depth of flow (outside the trickle channel area and main

channel area for sandy soils) for the 100-year flood peak shall be limited

to five feet in grass lined channels.

d.  Side Slopes

Side slopes shall be four (horizontal) to one (vertical) or flatter. Side

slopes for channels with 100-year runoff peaks of 20 cfs or less shall be

three (horizontal) to one (vertical) or flatter.

7.	Grass Lining

The grass lining for channels shall be in accordance with the UD&FCD Manual,

section 2.3.2, "Major Drainage - Grass Lined Channels -Grass"; and "Guidelines

for Development and Maintenance of Natural Vegetation".

8.	Erosion Control

The requirements for erosion control for grass lined channels shall be as

defined in the UD&FCD Manual, section 2.3.6, "Major Drainage Erosion Control."

The design of riprap and erosion control devices shall be in accordance with

section 411.1 and 411.2 of these Standards and Specifications.

9.	Hydraulic Information

Calculations of the capacity, velocity, and Froude numbers shall be submitted

with the construction drawings.

(c)	Concrete Lined Channels (Small Drainageways)

The criteria for the design and construction of concrete lined channels is presented

below:

1.	Hydraulics

a.  Freeboard

Adequate channel freeboard above the designed water surface shall be

provided and shall not be less than that determined by the following:

Hfb    = 2.0 = 0.025 V (d)1/3    (Equation 400-3)

where  Hfb     = freeboard height (feet)

V       = velocity (feet per second)

d       = depth of flow (feet)

Freeboard shall be in addition to superelevation, standing waves, and/or

other water surface disturbances. These special situations are to be

addressed in a Design Report to be submitted with the construction drawings

and specifications (subsection 402.5).

Concrete side slopes shall be extended to provide freeboard.

b.  Superelevation

Superelevation of the water surface shall be determined at all horizontal

curves, and design of the channel section adjusted accordingly.

c.  Velocities

Flow velocities shall not exceed 18 fps during the 100-year flood.

2.	Concrete Materials

A Design Report shall be prepared as stated in section 406.2(c). The minimum

concrete material specifications are as follows:

a.  Cement type: sulphate resistant.

b.  Minimum cement content: 500 lbs/C.Y.

c.  Maximum water-cement ratio: 0.50 (six gals. per sack).

d.  Maximum aggregate size: 1 1/2 inches.

e.  Air entrainment content: four to seven percent.

f.  Slump: two to four inches.

g.  Minimum compressive strength (f'c): 3750 psi at 28 days.

h.  Admixtures: All proposed admixtures shall be discussed in the Design

Report.

3.	Concrete Lining Section

a.  All concrete lining shall have a sufficient thickness to withstand the

structural and hydraulic loads.

b.  The side slopes shall be a maximum of two (vertical) to one (horizontal),

or a structurally reinforced wall if steeper.

4. 	Concrete Joints

a.  Expansion/contraction joints shall be installed where new concrete lining

is connected to a rigid structure or to existing concrete lining that is

not continuously reinforced.

b.  Longitudinal joints, where required, shall be constructed on the side walls

at the least one foot vertically above channel invert.

c.  All joints shall be designed to prevent differential movement.

d.  Construction joints are required for all cold joints and where the lining

thickness changes.

5.	Concrete Finish

The surface of the concrete lining shall be provided with a wood float finish.

Excessive working or wetting of the finish shall be avoided.

6.	Concrete Curing

All concrete shall be cured by the application of a liquid membrane forming

curing compound (white pigmented) upon completion of the concrete finish.

7.	Reinforcement Steel (where used)

a.  Steel reinforcement shall be minimum grade-40 deformed bars. Fabric mesh

may also be approved. Wire mesh shall not be used.

b.  Ratio of longitudinal steel area to concrete cross sectional area shall

be greater than .005.

c.  Ratio of transverse steel area to concrete cross sectional area shall be

greater than .0025.

d.  Additional steel as needed if a retaining wall structure is used.

8.	Earthwork

The following areas shall be compacted to at least 95 percent of maximum

density as determined by ASTM D-698 (Standard Proctor):

a.  The 12 inches of subgrade immediately beneath concrete lining (both

channel bottom and side slopes).

b.  Top 12 inches of maintenance road.

c.  All fill material.

9.	Bedding

Provide six inches of granular bedding equivalent in gradation to 3/4 inch

concrete aggregate (Standard Specifications for Road & Bridge Construction,

CDOT, latest revision) under channel bottom and side slopes.

10.	Underdrain

Longitudinal underdrains shall be provided and shall daylight at the check

drops. Weep holes shall be provided in vertical wall sections of the channel.

11.	Safety Requirements

a.  A six-foot high vinyl coated chain link, a comparable fence, or an

architecturally approved restraining device shall be installed to prevent

access wherever the 100-year channel flow depths exceed three feet.

Gates, with top latch, shall be placed at 250' intervals and staggered

where fence is required on both sides of the channel.

b.  Ladder-type steps shall be installed not more than 400 feet apart on

alternating sides of the channel depths in excess of three feet. Bottom

rung shall be placed approximately 12 inches vertically above channel

invert.

(d)	Riprap Lined Channels (Small Drainageways)

The criteria for the design and construction of riprap fabric lined channels, shall

be in accordance with the UD&FCD Manual, Volume 2, "Major Drainage - Riprap."

Riprap lined channels shall be designed for a turbulence factor (Froude number)

less than 0.8 for the 100-year flood peaks. The riprap shall be designed and

constructed in accordance with section 411.2 of these Standards and Specifications.

Freeboard requirements shall be in accordance with the standards for grass lined

channels defined in section 406.4(b) of these criteria.

(e)	Other Lining Types (Small Drainageways)

The criteria for the design of channels with linings other than grass, rock, or

concrete shall be dependent on the manufacturer's recommendations for the specific

product. The applicant shall be required to submit the technical data in support

of the proposed material. Additional information or calculations may be requested

by the City Engineer to verify assumptions or design criteria. The following

minimum criteria also shall apply.

1.	Flow Velocity

The maximum normal depth velocity shall be dependent on the construction

material used; however, the Froude number shall be less than 0.8.

2.	Freeboard

Refer to section 406.5(b).

3.	Curvature

The center line curvature shall have a minimum radius twice the top width of

the design flow but not less than 50 feet. The minimum radius of curvature for

channels with a 100-year runoff of 20 cfs or less shall be 25 feet.

4.	Roughness Coefficient

A Manning's "n" value range shall be established by the manufacturer's data,

with the high value used to determine depth/capacity requirements and the low

value used to determine Froude number and velocity restrictions.

5.	Cross Sections

Same as for grass lined channels, section 406.5(b).

406.6	Roadside Ditches

The criteria for the design of roadside ditches is similar to the criteria for grass

lined channels with modifications for the special purpose of minor storm drainage. The

criteria is as follows (refer to Figure 400-11):

(a)	Capacity

Roadside ditches shall have adequate capacity for the minor storm runoff peaks.

Capacity shall be as defined in Figure 400-48. Where the storm runoff exceeds the

capacity of the ditch, a storm sewer system shall be required.

(b)	Flow Velocity

The maximum velocity for the minor flood peak shall not exceed five feet per

second for Type-I ditch and 7.0 feet per second for Type-II or Type-III ditches.

(c)	Longitudinal Slope

The slope shall be limited by the average velocity of the minor flood peaks. Check

drops may be required where street slopes are in excess of two percent.

(d)	Freeboard

Freeboard shall be equal to the velocity head or a minimum of six inches.

(e)	Curvature

The minimum radius of curvature shall be 25 feet.

(f)	Roughness Coefficient

Manning's "n" values presented in Figure 400-7 shall be used in the capacity

computation for roadside ditches.

(g)	Grass Lining

The grass lining shall be in accordance with the UD&FCD Manual, Section 2.3.2.

(h)	Driveway Culverts

Driveway culverts shall be sized to pass the minor storm ditch flow capacity

without overtopping the driveway. The minimum size culvert shall be a 22 inches x

13 inches CMPA (18 inch equivalent round pipe) or equivalent with flared-end

sections. More than one culvert may be required.

(i)	Major Drainage Capacity

The capacity of roadside ditches for major drainage flow is restricted by the

maximum flow depth allowed at the street crown (subsection 403.4(d) of these

Standards and Specifications.

406.7	Channel Rundowns

A channel rundown is used to convey storm runoff from the bank of a channel to the

invert of an open channel or drainageway. The purpose of the structure is to minimize

channel bank erosion from concentrated overland flow. The design criteria for channel

rundowns is as follows:

(a)	Cross-Sections

Typical cross-sections for channel rundowns are presented in Figure 400-13.

(b)	Design Flow

The channel rundown shall be designed to carry a minimum of the minor storm runoff

of 1 cfs, whichever is greater.

(c)	Flow Depth

The maximum depth at the design flow shall be 12 inches. Due to the typical profile

of a channel rundown beginning with a flat slope and then dropping steeply into the

channel, the design depth of flow shall be the computed critical depth for the

design flow.

(d)	Outlet Configuration

The channel rundown outlet shall enter a drainageway at the trickle channel

flowline. Erosion protection of the opposite channel bank shall be provided by a

24-inch layer of grouted Type-L riprap. The width of this riprap erosion protection

shall be at least three times the channel rundown width or pipe diameter. Riprap

protection shall extend up the opposite bank to the minor storm flow depth in the

drainageway or two feet, whichever is greater.

406.8	Checklist

To aid the designer and reviewer, the following checklist has been prepared.

1.	Check flow velocity with low retardance factor and capacity with high retardance

factor.

2.	Check Froude number and critical flow conditions.

3.	Grass channel side slopes must be 4:1 or flatter except for roadside ditches that

shall be 3:1 or flatter unless approved by the City.

4.	Show energy grade line and hydraulic grade line on design drawings.

5.	Consider all backwater conditions (i.e., at culvert) when determining channel

capacity.

6.	Check velocity for conditions without backwater effects.

7.	Provide adequate freeboard.

8.	Provide adequate ROW for the channel and continuous maintenance access.

407	STORM SEWERS

407.1	Introduction

Storm sewers are a part of the Minor Drainage System, and are required when the other

parts of the minor system, primarily curb, gutter, and roadside ditches no longer have

capacity for additional runoff.

Except as modified herein, the design of storm sewers shall be in accordance with the

UD&FCD Manual Section on "Storm Sewers." Reference is made to follow specific sections

in the UD&FCD Manual for clarity. The user is referred to the UD&FCD Manual and other

references cited for additional discussion and basic design concepts.

A computer program for the design of a storm sewer system shall be permitted provided

the model is calibrated to three or more design points using the procedures presented

in these criteria. Contact the City Engineer for specific information required.

407.2	Construction Materials

All storm sewers within the City shall be constructed using one of the following

materials and meet the applicable standard as presented below:

TABLE 400-7

STORM SEWER STANDARDS

Pipe Material               Standard

Reinforced Concrete         ASTM C-76/C-506/C-507/C-789/C-850 or

AASHTO M-170/M-206/M-207/M-259/M-273

Plastic Pipe                AASHTO design (only as approved by City)

The minimum class for RCP pipe shall be Class-II. The required pipe strength shall be

determined from the actual depth of cover, true load, and proposed field conditions. A

typical design strength calculation shall be submitted to the City for approval.

407.3	Hydraulic Design

Storm sewers shall be designed to convey the minor storm flood peaks without surcharging

the sewer. To ensure that this objective is achieved, the hydraulic and energy grade

lines shall be calculated by accounting for pipe friction losses and pipe form losses.

Total hydraulic losses shall include friction, expansion, contraction, bend, and junction

losses. The methods for estimating these losses are presented in the following sections.

The final energy grade line shall be at or below the proposed ground surface.

(a)	Pipe Friction Losses

The Manning's "n" values to be used in the calculation of storm sewer capacity and

velocity are presented in Figure 400-14.

(b)	Pipe Form Losses

Generally, between the inlet and outlet the flow encounters a variety of

configurations in the flow passageway such as changes in pipe size, branches,

bends, junctions, expansions, and contractions. These shape variations impose

losses in addition to those resulting from pipe friction. Form losses are the

result of fully developed turbulence and can be expressed as follows:

Hl = K [V2]

[2g]

where Hl = head loss (feet)

K = loss coefficient

[V2] = velocity head (feet)

2g

g = gravitational acceleration (32.2ft/sec2)

The following is a discussion of a few of the common types of form losses

encountered in sewer system design.

1.	Expansion Losses

Expansion in a storm sewer conduit shall result in a shearing action between

the incoming high velocity jet and the surrounding sewer boundary. As a

result, much of the kinetic energy is dissipated by eddy currents and

turbulence. The loss of head can be expected as

(Equation 400-5)

Hl = Ke [V1 2] [1 - A1]

[ 2g ] [    A2]

in which A is the cross section area, V is the average flow velocity, and K is

the loss coefficient. Subscripts 1 and 2 denote the upstream and downstream

sections, respectively. The value K is about 1.0 for a sudden expansion, and

about 0.2 for a well designed expansion transition. Figure 400-15 presents the

expansion loss coefficients for various flow conditions.

2.	Contraction Losses

The form loss due to contraction is:

(Equation 400-6)

Hl = Kc [V2 2] [1 - [A2] 2] 2

[ 2g ] [    [A1]  ]

where Kc is the contraction coefficient, Kc is equal to 0.5 for a sudden

contraction and about 0.1 for a well designed transition. Subscripts 1 and 2

denote the upstream and downstream sections, respectively. Figure 400-15

presents the contraction loss coefficient for various flow conditions.

3.	Bend Losses

The head losses for bends, in excess of that caused by an equivalent length

of straight pipe, may be expressed by the relation

(Equation 400-7)

Hl = Kb [V2]

[2g]

in which Kb is the bend coefficient. The bend coefficient has been found to

be a function of, (a) the ratio of the radius of curvature of the bend to the

width of the conduit, (b) deflection angle of the conduit, (c) geometry of the

cross section of flow, and (d) the Reynolds number of relative roughness. A

table showing the recommended bend loss coefficients if presented in Figure

400-16 and 400-17.

4.	Junction and Manhole Losses

A junction occurs where one or more branch sewers enter a main sewer, usually

at manholes. The hydraulic design of a junction is in effect the design of

two or more transitions, one for each flow path. Allowances should be made for

head loss due to the impact at junctions. The head loss for a straight through

manhole or at an inlet entering a storm sewer (Case I on Figure 400-18 is

calculated using Equation 400-4.

The head loss for a junction with one or more laterals (Case II and III on

Figure 400-18 is calculated using Equation 400-8):

(Equation 400-8)

Hl = V2 2 - Kj [V1 2]

2g         2g

where V2 is the outfall flow velocity and V1 is the inlet velocity. The loss

coefficient, Kj, for various junctions is presented in Figure 400-18.

(c)	Storm Sewer Outlets

When the storm sewer system discharges into the Major Drainageway System (usually

an open channel), additional losses occur at the outlet in the form of expansion

losses (refer to Section 406.3(b)). For a headwall and no wingwalls, the loss

coefficient Ke = 1.0 (refer to Figure 400-15), and for a flared-end section the

loss coefficient is approximately 0.5.

(d)	Partially Full Pipe Flow

When a storm sewer is not flowing full, the sewer acts like an open channel, and

the hydraulic properties can be calculated using open channel techniques (refer

to subsection 406). For convenience, charts for various pipe shapes have been

developed for calculating the hydraulic properties (Figures 400-20, 400-21, and

400-22). The data presented assumes that the friction coefficient, Manning's

"n" value, does not vary throughout the depth.

(e)	Hydraulic Research

The American Public Works Association (APWA) has conducted research into the

head losses at various junctions and manholes. The work consisted of

experimentally modelling three types of sewer junctions: junctions with a 90

degree bend, junctions of a main with a perpendicular lateral, and junctions of

two opposed laterals. The work was primarily directed at sanitary sewers because the

sizes investigated (i.e., manhole diameter to sewer diameter ratio of 2.3 to 4.6)

and the flow conditions (i.e., pressure flow) were typical for sanitary sewers.

However, several trends were observed that are considered to be suitable for storm

sewers, including specific energy loss coefficients that have been adopted for

these criteria. The trends observed from the test results are as follows:

1.	For manhole diameter to sewer diameter ratios between two and six, the

variation in head loss was insignificant.

2.	The most significant reduction in head loss occurs when the manhole is

shaped by benching the bottom of the manhole up to the top of the pipe. This

appears to provide a better channelization of the flow, which reduces the

losses.

3.	Some testing was also performed for open channel flow conditions. These tests

generally showed that the energy losses were less than for pressure flow.

Since most storm sewers are not pressurized, the use of the coefficients should

be conservative.

This information is presented to aid the designer in selecting suitable energy loss

coefficients for situations not covered by these criteria.

407.4	Vertical Alignment

The sewer grade shall be such that a minimum cover is maintained to withstand AASHTO

HS-20 (or as designated by the City Engineer) loading on the pipe. The minimum cover

depends upon the pipe size, type and class, and soil bedding condition, but shall be

not less than 18-inches at any point along the pipe.

See City Standard Utility Specifications for more information on the next two paragraphs.

The minimum clearance between storm sewer and water main, either above or below, shall be

18-inches. Additional protection of the water line or storm sewer shall be required for

clearances of 18-inches or less.

The minimum clearance between storm sewer and sanitary sewer, either above or below,

shall also be 18-inches. In addition, when a sanitary sewer main lies above a storm

sewer, or within 18-inches below, the sanitary sewer shall be constructed of structural

sewer pipe (with encased pipe joints when crossing water lines) for a minimum of 10-feet

on each side of where the storm sewer crosses.

407.5	Horizontal Alignment

Storm sewer alignment may be curvilinear for pipe with diameters of 48-inches or

greater but only when approved in writing by the City Engineer. The applicant must

demonstrate the need for a curvilinear alignment. Generally, a curvilinear alignment

shall only be allowed where physical constraints dictate the use of a curvilinear

alignment. The limitations on the radius for pulled-joint pipe is dependent on the

pipe length and diameter, and amount of opening permitted in the joint. The maximum

allowable joint shall be 3/4 inches. The minimum parameters for radius type pipe is

shown in Figure 400-14. The radius requirements for pipe bends is dependent upon the

manufacturer's specifications.

The minimum horizontal separation between storm sewers or sanitary sewers and water

lines will be 10 feet.

407.6	Pipe Size

The minimum allowable pipe size for storm sewers except for detention outlets shall be

18" diameters and shall be rounded pipe. The length of the sewer also affects the

maintenance and, therefore, the minimum diameter. Figure 400-14 presents the minimum

pipe size for storm sewers.

407.7	Manholes

Manholes or maintenance access ports shall be required whenever there is a change in

size, direction, elevation, grade, or where there is a junction of two or more sewers.

A manhole may be required at the beginning and/or at the end of the curved section of

storm sewer. The maximum spacing between manholes for various pipe sizes shall be in

accordance with Figure 400-14. The required manhole size shall be as follows:

SEWER                    MANHOLE

DIAMETER                 DIAMETER

15" to 18"               4'

21" to 42"               5'

48" to 54"               6'

60" and larger           CDOT Std. M-604-20 and M-604-21

Larger manhole diameters or a junction structure may be required when sewer alignments

are not straight through or more than one sewer line goes through the manhole.

407.8	Design Example

The following calculation example, including the calculation Figure 400-19 and Figures

400-23 and 400-24 were obtained from Modern Sewer Design, AISI, Washington, D.C., 1980

and edited for the calculation of manhole and junction losses in accordance with this

Section.

EXAMPLE 1:  HYDRAULIC DESIGN OF STORM SEWERS

Given:      (a)  Plan and Profile of storm sewer (Figures 400-23 and 400-24).

Example calc form (Figure 400-19).

(b)  Station 0+00 (outfall) data as follows:

Design discharge              Q    = 145 cfs            [9]

Invert of pipe                     = 94.50'             [2]

Diameter                      D    = 66" RCP            [3]

Starting water surface        W.S. = 100'               [4]

Area of pipe                  A    = 23.76 sq. ft.      [6]

Q          V    = 6.1 f/s            [8]

Velocity =         A

Note:  (1)         Number in brackets refers to the columns on Figure 400-19

(2)         Sizes of the storm sewer were determined during the

preliminary design phases

FIND:       Hydraulic Grade Line and Energy Grade Line for storm sewer.

DISCUSSION: The following procedure is based on full-flow pipe conditions. If the

pipe is flowing substantially full (i.e., greater than 80 percent),

the following procedures can be used with minimal loss of accuracy.

However, the designer is responsible for checking the assumptions

(i.e., check for full flow) to assure that the calculations are

correct.

STEP 1:     The normal depth is greater than critical depth, dn > dc; therefore,

calculations to begin at outfall, working upstream. Compute the

following parameters:

O = 2gn2 = 2 x 32.2 x (.013)2

2.21          2.21

This equation is derived from the Manning's equation by solving for

velocity and converting to velocity head.

O = 0.00492

This value remains constant for this design since the n-value does

not change.

STEP 2:     Velocity head [10]:

Hv = V2 =  (6.1)2

2g   (2)(32.2)

Hv = 0.58

STEP 3:     Energy Grade Point, E.G. [11]:

E.G. = W.S. + Hv = 100 + 0.58

E.G. = 100.58

For the initial calculation, the Energy Grade Line is computed as

described above. For subsequent calculations, the equation is reversed,

and the water surface is calculated as follows (see Step 12):

W.S. = E.G. - Hv

This equation is used since the losses in Step 8 are energy losses which

are added to the downstream energy grade elevation as the new starting

point from which the velocity head is subtracted as shown above.

STEP 4:     Sf = O Hv = (.00492)(0.58)

R4/3    (1.375)4/3

Sf = .0019

NOTE: R = the hydraulic radius of the pipe.

STEP 5:     Avg. Sf [13]:    Average skin friction: This is the average value

between Sf of the station being calculated and the

previous station. For the first station, Avg. Sf =

Sf. Beginning with Column 13, the entrees are placed

in the next row since they represent the calculated

losses between two stations.

STEP 6:     Enter sewer length, L, in column 14

STEP 7:     Friction loss Hf [15]:    Hf = (Avg. Sf)(L)

Hf = (0.0019)(110)

Hf = 0.21

STEP 8:     Calculate the form losses for bends, junctions, manholes, and transition

losses (expansion or contraction) using equations 400-4, 400-5, 400-6,

400-7, and 400-8. The calculation of these losses is presented below for

the various sewer segments, since all the losses do not occur for one

sewer segment.

(a)    station 1 + 10 to 1 + 52.4 (bend)

Hb = Kb Hv, where the degree of bend is 60 degrees

Kb = 0.20 (Figure 400-16, Case I)

Hb = (0.20) (0.58) = 0.12, enter in column 16

(b)    station 2 + 48 to 2 + 55.5 (transition: expansion)

Hl = Ke Hv-1 [1 - [A1] ]2

[    [A2] ]

Ke = 1.06 (Figure 400-15) for D2/D1 = 1.5, and O = 45

Hl = (1.06) 1.29 [1 - [15.9 ] ]2

[    [23.76] ] = 0.15, enter in column 19

(c)    station 3 + 55.5 (manhole, straight through)

Hm = Km Hv

Km = 0.05 (Figure 400-18, Case I)

Hm = (0.05) (1.29) = 0.06, enter in column 18

(d)    station 4 + 55.5 to 4 + 65.5 (junction)

Hj = Hv-2 - Kj Hv-1

Kj = 0.62 (Figure 400-8, Case III), O = 30 degrees

Hj = 1.29 - (6.2) (0.99) = 0.68, enter in column 17

(e)    station 5 + 65.5 to 5 + 75.5 (junction) - since there are two

laterals, the loss is estimated as twice the loss for one lateral

Kj = 0.33 (Figure 400-18, Case II), O = 70 degrees

Hj = 0.99 - (0.33) (0.64) = 0.78 for one lateral

STEP 9:     Sum all the form losses from columns 15 through 19 and enter in column

20. For the reach between Station 0+00 to 1+00, the total loss is 0.21.

STEP 10:    Add the total loss in column 20 to the energy grade at the downstream

end (Sta. 0+0) to compute the energy grade at the upstream end (Sta.

1+0) for this example).

E.G. (U/S)    = E.G. (D/S) + TOTAL LOSS

= 100.58 + 0.21

= 100.79 (Column 11)

where  E.G.    = energy grade

U/S     = upstream

D/S     = downstream

STEP 11:    Enter the new invert [2], pipe diameter D[3], pipe shape [5], pipe area

A, [6], the compute constant c from Step 1 in column [7], the computed

velocity V in column [8], the new Q [9], and the computed velocity head

Hv [10].

STEP 12:    Compute the new water surface, W.S., for the upstream station (1+10 for

this example).

W.S.    = E.G. - Hv

= 100.79 - 0.58

= 100.21 (column 4)

STEP 13:    Repeat Steps 1 through 12 until the design is complete. The hydraulic

grade line and the energy grade line are plotted on the profile (Figure

400-24).

DISCUSSION OF RESULTS:

The Hydraulic Grade Line (HGL) is at the crown of the pipe from Station 0+00 to

2+48. Upstream of the transition (Station 2+55.5) the 54 inch RCP has a greater

capacity (approximately 175 cfs) at the slope than the design flow (145 cfs). The

pipe is therefore not flowing full but is substantially full (i.e., 145/175 = 0.84

greater than 0.80). The computed HGL is below the crown of the pipe. However, at

the outlet, the actual HGL is higher, since the outlet of the 54 inch RCP is

submerged by the headwater for the 66 inch RCP. To compute the actual profile, a

backwater calculation would be required; however this accuracy is not necessary

for storm sewer design in most cases.

At the junction (Station 4+55.5), the HGL is below the top of the pipe. However,

in this case, the full flow capacity (100 cfs) is the same as the design capacity;

and the HGL remains parallel to the top of the pipe. A similar situation occurs at

the junction at Station 5+65.5 except that the HGL remains above and parallel to

the top of the pipe.

If the pipe entering a manhole or junction is at an elevation significantly above

the manhole invert, a discontinuity in the EGL may occur. If the EGL of the

incoming pipe for the design flow condition is higher than the EGL in the manhole,

then a discontinuity exists, and the higher EGL is used for the incoming pipe.

407.9	Checklist

To aid the designer and reviewer, the following checklist has been prepared:

(1)	Calculate energy grade line (EGL) and hydraulic grade line (HGL) for all sewers

and show on the construction drawings or on a separate copy of the plans submitted

with the construction drawings.

(2)	Account for all losses in the EGL calculation including outlet, form, bend, manhole,

and junction losses.

(3)	Provide adequate protection at the outlet of all sewers into open channels.

(4)	Check for minimum pipe cover and clearance with utilities.

408	STORM SEWER INLETS

408.1	Introduction

There are three types of inlets: curb opening, grated, and combination inlets. Inlets are

further classified as being on a "continuous grade" or in a sump. The term "continuous

grade" refers to an inlet so located that the grade of the street has a continuous slope

past the inlet and, therefore, ponding does not occur at the inlet. The sump condition

exists whenever water is restricted or ponds because the inlet is located at a low point.

A sump condition can occur at a change in grade of the street from positive to negative,

or at an intersection due to the crown slope of a cross street.

Presented in this chapter is the criteria and methodology for design and evaluation of

storm sewer inlets in the City. Except as modified herein, all storm sewer inlet criteria

shall be in accordance with the UD&FCD Manual.

408.2	Standard Inlets

(a)	Types of Inlets

The standard inlets permitted for use in the City are:

TABLE 400-8

STANDARD INLET TYPE

TYPE                 DETAIL                   PERMITTED USE

Curb Opening Inlet   CDOT Standard            All street types with vertical

Type R               M-604-12                 curb (lengths of 5', 10', then 1'

increments)

Grated Area Inlet    CDOT Standard            Parking lots and open area sumps.

Type 13 or Type C    M-604-13,

M-604-10

*Note: Combination inlets may be requested as a variance with proper justification

to the City Engineer for approval.

(b)	Use Limitations

Inlets and inlet transitions are prohibited in curb returns, driveways, and street/

curb transitions.

408.3	Inlet Hydraulics

The procedure and basic data used to define the capacities of the standard inlets under

various flow conditions were obtained from the UD&FCD Manual, Volume 1, Section on "Storm

Inlets," for curb opening inlets. The procedure consists of defining the amount and

depth of flow in the gutter and determining the theoretical flow interception by the

inlet. To account for effects which decrease the capacity of the various types of inlets,

such as debris plugging, pavement overlaying, and variations in design assumptions, the

theoretical capacity calculated for the inlets is reduced to the allowed capacity by the

factors presented below for the standard inlets.

TABLE 400-9

ALLOWABLE INLET CAPACITY

PERCENTAGE OF

THEORETICAL CAPACITY

CONDITION                    INLET TYPE                    ALLOWED

Sump of Continuous Grade     CDOT Type R (M-604-12)

5' length                          88

10' length                         92

15' length                         95

Continuous Grade          CDOT Grated Type 13 (M-604-13)        60

Sump  	                CDOT Grated Type 13 (M-604-13)        50

Allowable standard inlet capacities for the minor and major storm inlets have been

developed and are presented in the following figures:

REFER TO FIGURES

INLET TYPE    FLOW CONDITION    (Minor Storm)

Type R        Continuous Grade  Figure 400-26

Type R        Sump              Figure 400-27

Type 13       Continuous Grade  Figure 400-25

Type 13       Sump              Figure 400-27

These figures include the reduction factors in the above table. The allowable inlet

capacity is compatible with the allowable street capacity, (refer to subsection 409).

The values shown were calculated on the basis of the maximum flow allowed in the street

gutter. For the gutter flow amounts less than the maximum, the allowable inlet capacity

must be proportionately reduced.

(a)	Continuous Grade Condition

For the "continuous grade" condition, the capacity of the inlet is dependent upon

many factors including gutter slope, depth of flow in the gutter, height and length

of curb opening, street cross slope, and the amount of depression at the inlet. In

addition, all of the gutter flow shall not be intercepted and some flow shall

continue past the inlet area ("inlet carryover"). The amount of carryover must be

included in the drainage facility evaluation as well as in the design of the inlet.

The use of Figures 400-26 and 400-27 is illustrated by the following examples:

Example 2:    Design of Type R Curb Opening Inlets (Minor Storm)

Given:        Street Type = Arterial - 6 Lane, S = 1.0 percent

Maximum flow depth = 0.5 feet (refer to Section 409.4)

Maximum allowable gutter capacity = 11.0 cfs (refer to Section 409.4)

Starting gutter flow (Q1) = 8.0 cfs

Find:         Interception and carryover amounts for the inlets and flow conditions

illustrated on figure 400-28.

Solution:     From figure 400-28 we can see that inlets 1 and 2 are in a continuous

grade condition and inlet 3 is in a sump condition. The first step is

to calculate the interception ratio R, for the continuous grade

inlets. This ratio is then applied to the actual gutter flow (local

runoff plus carryover flow) to determine amount intercepted by the

inlet and the carryover flow. The final step is to calculate the

size of the inlet required for the sump condition, discussed in

Example #3 in the following section.

Step 1:       From Figure 400-26 for an allowable depth of 0.50 feet and a 15'

inlet, read the value 8.6 cfs. Note that even though the gutter flow

is less than maximum allowable, the maximum depth is used for Figure

400-30. The effect of the lower depth on the inlet capacity shall be

accounted for in the following steps.

Step 2:       Compute the interception ratio R

R =    Allowable Inlet Capacity = 8.6

Allowable Street Capacity 11.0

R = 0.78

Step 3:       Compute the interception amount Qi

Qi =   R x Q street

=   0.78 x 8.0

Qi =   6.2 cfs amount intercepted by inlet

Step 4:       Qco =  Q street = Qi

=  8.0 - 6.2

Qco =  1.8 cfs

Step 5:       Compute the total flow at the next inlet, which is the sum of the

carryover (Qco) from inlet #1 plus the local runoff to inlet #2

Qt (inlet #2) =  Qco (inlet #1) + Qi (inlet #2)

=  1.8 cfs + 4 cfs

Qt (inlet #2) =  5.8 cfs

Step 6:       Compute the interception ratio, intercepted amount, and carryover

flow for inlet #2 using the procedure described in steps 1 through 4

Allowable inlet capacity = 7.2 cfs  Fig 400-26

R = (7.2 cfs)(11.0cfs) = 0.65

Qi (inlet #2) = (0.65)(5.8 cfs) = 3.8 cfs

Qco (inlet #2) = 5.8 cfs = 2.0 cfs

Step 7:       Compute the inlet #2 using the procedures described in step 5

Qt (inlet #3) = 8 cfs + 2.0 cfs = 10.0 cfs

Step 8:       Size the inlet in the sump condition using the procedures described

in Example #3, section 408.3(b) and Figure 400-27. For this example,

with an allowable maximum depth of flow of 0.5 cfs, a 10-foot Type R

inlet shall intercept more than the total gutter flow and is therefore

acceptable.

(b)	Sump Condition

The capacity of the inlet in a sump condition is dependent on the depth of ponding

above the inlet. Typically the problem consists of estimating the number of inlets

or depth of flow required to intercept a given flow amount. The use of Figure 400-

27 is illustrated by the following example:

Example 3:    Allowable Capacity for Type 13 Inlet in a Sump (Minor Storm)

Given:        Flow = 8.0 cfs

Maximum allowable street depth = 0.50 feet

Type 13 double inlet

Find:         Depth of ponding

Solution:

Step 1:  From Figure 400-27 read the "Depth of Ponding" for double Type 13 inlet as

D = 0.28' at the gutter flow of 8.0 cfs (inlet capacity)

Step 2:  Compare computed to allowable depth. Since the computed depth is less than

the allowable depth, the inlet is acceptable, otherwise the amount of

inlets or the type of inlet would be changed and the procedure repeated.

408.4	Inlet Spacing

The optimum spacing of storm inlets is dependent upon several factors including traffic

requirements, contributing land use, street slope, and distance to the nearest outfall

system. The suggested sizing and spacing of the inlets is based upon the interception

rate of 70 percent to 80 percent. This spacing has been found to be more efficient than

a spacing using 100 percent interception rate. Using the suggested spacing only, the

most downstream inlet in a development would be designed to intercept 100 percent of

the flow. Also, considerable improvements in over-all inlet system efficiency can be

achieved if the inlets are located in the sumps created by street intersections. The

following example illustrates how inlet sizing and interception capacity may be analyzed:

Example 4:    Inlet Spacing

Given: 	    Maximum allowable street flow depth = 0.50 ft.

Street slope = 1.0 percent

Maximum allowable gutter flow = 11.0 cfs

Gutter flow = 11.0 cfs

Find:         Size and type of inlet for 75 percent interception

Solution:

Step 1:	    Compute desired capacity

Q = (0.75)(11.0 cfs) = 8.3 cfs

Step 2:  	    Read the allowable inlet capacities from Figure 400-25 and 400-26 for

various inlets. The following values were obtained:

INLET TYPE          CAPACITY          PERCENT INTERCEPTION

Double Type R       7.2 cfs                    66

Triple Type R       8.6 cfs                    78

Therefore, a curb opening inlet Type-R, L = 15 feet is required and shall

intercept 8.6 cfs. The remaining 2.4 cfs shall continue downstream and

contribute to the next inlet. Spacing between such inlets shall depend on

the local runoff, and the amount of flow bypassed at the upstream inlet.

A comparison of the inlet capacity with the allowable street capacity

(refer to section 409) shall show that the percent of street flow

interception by the inlets varies from less than 50 percent to as much as

95 percent of the allowable street capacity. Therefore, the optimum inlet

spacing cannot be achieved in all instances, and the spacing requirements

should be analyzed by the design engineer.

408.5	Checklist

To aid the designer and reviewer, the following checklist has been prepared:

1.	Check the inlet capacity to determine the carryover flow, and account for this

flow plus the local runoff in the sizing of the next downstream inlet.

2.	Place inlets at the flattest grade or in sump conditions where possible to increase

capacity.

3.	Space inlets based upon the interception rate of 70 percent to 80 percent of the

gutter flow to optimize inlet capacity.

409	STREETS

409.1	Introduction

The criteria presented in this subsection shall be used in the evaluation of the

allowable drainage encroachment within public streets. The review of all planning

submittals (refer to subsection 402) shall be based on the criteria herein.

409.2	Function of Streets in the Drainage System

Urban and rural streets, specifically the curb and gutter or the roadside ditches, are

part of the Minor Drainage System. When the drainage in the street exceeds allowable

limits (refer to subsection 403.4(d), a storm sewer system or an open channel is

required to convey the excess flows. The streets are also part of the Major Drainage

System when they carry floods in excess of the minor storm (refer to subsection

403.4(b), also subject to certain limitations (refer to subsection 403.4(d).

However, the primary function of urban streets is for traffic movement and, therefore,

the drainage function is subservient and must not interfere with the traffic function

of the street.

Design criteria for the collection and moving of runoff water on public streets is

based on a reasonable frequency and magnitude of traffic interference. That is, depending

on the character of the street, certain traffic lanes can be fully inundated once during

the minor design storm return period. However, during lesser intense storms, runoff shall

also inundate traffic lanes but to a lesser degree. The primary function of the streets

for the Minor Drainage System is therefore to convey the nuisance flows quickly and

efficiently to the storm sewer or open channel drainage without interference with traffic

movement. For the Major Drainage System, the function of the streets is to provide an

emergency passageway for the flood flows with minimal damage to urban environment.

409.3	Street Classification

The streets in the City are classified for drainage use as Type A, B, or C according to

the average daily traffic (ADT) for which the street is designed. The larger the ADT, the

more restrictive the allowable drainage encroachment into the driving lanes. The limits

of storm runoff encroachment for each Drainage Classification and storm condition is set

forth under subsection 403.4(d).

409.4	Hydraulic Evaluation

(a)	Allowable Capacity - Minor Storm

Based upon the policy of subsection 403.4(d) and the Drainage Classification of each

street in section 409 the allowable minor storm capacity of each street section is

calculated using the modified Manning's formula.

Q = (0.56) (Z/n) S1/2 Y8/3          (Equation 400-9)

where Q = discharge in cfs

Z = 1/Sx, where Sx is the cross slope of the pavement

Y = depth of water at face of curb (feet)

S = longitudinal grade of street (ft/ft)

n = Manning's roughness coefficient

The solution to the above equation can also be obtained through the use of the

nomograph of Figure 400-29 that is included for information only.

The allowable gutter capacity for each street cross section has been calculated

and is presented in Figure 400-31. The calculations were performed for various

allowable theoretic flow depths and street slopes. A Manning's n-value of 0.016

was used for the calculations at all street slopes. The allowable gutter capacity

was computed by multiplying the theoretical street capacity by the appropriate

reduction factor shown on Figure 400-30. The purpose of the reduction factor is

to account for various street conditions which decrease the street capacity. The

conditions include street overlays, parked vehicles, debris and hail accumulation,

and deteriorated pavement. The reduction factor also is used to minimize damaging

gutter flow velocities.

The allowable gutter capacity was computed using a symmetrical street section.

Therefore, the allowable gutter capacity shall need to be reduced for non-

symmetrical street sections. Street capacity calculations shall be submitted to

the City at critical locations of the non-symmetrical streets. This computed street

capacity must never exceed the allowable street capacity presented in these

criteria. The use of Figure 400-31 is illustrated by an example in section 409.5.

(b)	Allowable Capacity - Major Storm

The allowable street capacity for the major storm is calculated using the Manning's

formula by first dividing the street cross section into the pavement area and

sidewalk/grass area and then computing the individual flow contributions. The

capacity is subject to the limitations set forth in subsection 403.4(d) and the

drainage classification of section 409. The capacity calculations were performed

for each street cross section and published in a Technical Memorandum on file with

the City. The calculations were performed for various street slopes and plotted in

Figure 400-32. A Manning's n-value of 0.016 for the pavement area sand 0.025 for the

sidewalk/grass area was used to determine the capacity. The backslope from the curb

was assumed to be 2 percent. The maximum allowable depth at the gutter is 12 inches

(section 403.4(d)). For not-symmetrical streets (see Figure 400-33), street

capacity calculations shall be submitted to the City at critical locations. This

computed street capacity must never exceed the allowable street capacity presented

in these criteria. The use of Figure 400-32 is illustrated by an example in section

409.5.

(c)	Rural Streets

Rural streets are characterized by roadside ditches rather than curb and gutters for

urban streets. The capacity is limited by the depth in the ditch and the maximum

flow velocity. Refer to section 406.6(e) for the design and capacity of roadside

ditches.

409.5	Design Example

Example 5:    Determination of Street Capacity

Given:        Street with a traffic classification of "Arterial" and slope of one

percent.

Find:         Maximum allowable capacity for minor and major storm.

Solution:

Step 1:       Determine maximum allowable depth:

From Section 409.3 for a "Collector," read the

drainage classification as a Type C street. The maximum allowable theoretic

depth for the initial storm is 0.50 feet.

Step 2:	    Determine the allowable minor storm gutter capacity:

From Figure 400-31, for a "Arterial" with an allowable theoretic depth of

0.50 feet and a slope of one percent, read the allowable gutter capacity of

11.00 cfs. The flow velocity can also be obtained from Figure 400-31 by

interpolating between the velocity lines (V = 3.0 fps).

Step 3:	    Determine the allowable major storm gutter capacity:

From Figure 400-32 for a "Arterial" with a slope of one percent, read the

allowable capacity of 110 cfs per gutter assuming the street is

symmetrical. If the street cross section is not symmetrical (i.e., one

gutter flowline higher than the other), the capacity of the upper gutter

would have to be reduced so that the lower gutter capacity is not exceeded

by street cross flow from the upper gutter (see Figure 400-33).

409.6	Checklist

To aid the designer and reviewer, the following checklist has been prepared:

(1)	Use the flattest street slope to calculate the allowable gutter capacity.

(2)	Determine street classification first, then allowable depth and gutter capacity.

(3)	Non-symmetrical street evaluation.

(4)	Storm sewer required for gutter capacity exceedance.

(5)	Check adequacy of downstream facilities.

410	CULVERTS

410.1	Introduction

A culvert is defined as a conduit for the passage of surface drainage water under a

highway, railroad, canal, or other embankment (except detention outlets). Culverts may be

constructed with many shapes and materials. Reinforced concrete pipe (RCP) is available

in round, elliptical, or arch cross sections, in sizes ranging from 12 inches to 108

inches in diameter. The pipe also may be cast-in-place, although this construction

method is generally only used for storm sewers.

Corrugated Metal Pipe (CMP) and Aluminum Pipe culverts are available in round or arch

cross sections. Sections of corrugated metal also can be bolted together to form several

other cross sectional shapes, such as elliptical and pear shapes, forming structural

plate pipe (SPP). Corrugations also come in various dimensions, which affect the

hydraulics of the pipe flow.

Reinforced Concrete Box Culverts (RCBC) can be constructed with generally any rectangular

cross section, the only limitations being the physical site constraints and the

structural requirements. Precast box culverts are also available in several standard

dimensions.

Polyvinyl chloride (PVC) or other approved plastic pipe can be used with written approval

for each case by the City Engineer.

410.2	Culvert Hydraulics

The procedures and basic data to be used for the hydraulic devaluation of culverts in the

City shall be in accordance with the UD&FCD Manual Volume-2m "Inlets and Culverts,"

Section-2, "Hydraulics," except as modified herein. The reader is also referred to the

many texts covering the subject for additional information.

410.3	Culvert Design Standards

(a)	Construction Material and Pipe Size

Within the City, culverts shall be constructed from aluminum, concrete or corrugated

metal. Other materials for construction shall be subject to written approval by the

City Engineer.

The minimum pipe size for culverts within a public ROW shall be 24 inches diameter

round culvert, or shall have a minimum cross sectional area of 2.8 ft. for arch

shapes, and 3.3 ft. for elliptical shapes. Roadside ditch culverts for driveways

shall be 18-inches diameter round culvert or shall have a minimum cross sectional

area of 1.6 ft.

(b)	Inlet and Outlet Configuration

Within the City, all culverts are to be designed with headwalls and wingwalls, or

with flared-end sections at the inlet and outlet. Flared-end sections are only

allowed on pipes with diameters of 42-inches (or equivalent) or less.

Additional protection in the form of riprap shall also be required at the inlet

and outlet due to the potential scouring velocities. Refer to sections 411.2 and

411.3.

(c)	Hydraulic Data

When evaluating the capacity of a culvert, the following data shall be used:

1.	Roughness Coefficient      - Figure 400-34

2.	Entrance Loss Coefficients - Figure 400-35

3.	Capacity Curves - There are many charts, tables, and curves in the literature

for the computation of culvert hydraulic capacity. To assist in the review of

the culvert design computations and to obtain uniformity of analysis, the

following data shall be used:

All Culverts:    Urban Storm Drainage Criteria Manual, DRCOG, Denver, Colorado

1969 - Vol. 2, "Inlets and Culverts" section with all addenda

Concrete Pipe:   Concrete Pipe Design Manual, ACPA, Arlington, Virginia

February, latest additions

Corrugated Metal Pipe:  "Handbook of Steel Drainage and Highway Construction

Products," AISI, Washington, D.S., latest additions

Copies of the product manuals may be obtained through the local pipe suppliers.

4.	Design Forms - Standard Form SF-4, as shown in Figure 400-37, is to be used

for determining culvert capacities. A sample computation is discussed in

subsection 410.4 and shown on Figure 400-37.

(d)	Velocity Considerations

In design of culverts, both the minimum and maximum velocities must be considered.

A minimum velocity of flow is required to assure a self-cleansing condition of the

culvert. A minimum velocity in the culvert of three feet per second at the outlet

is recommended.

The maximum velocity is dictated by the channel conditions at the outlet. If the

outlet velocities are less than 7-fps for grassed channels, then the minimum

amount of protection is required due to the eddy currents generated by the flow

transition. Higher outlet velocities shall require substantially more protection.

A maximum outlet velocity of 12-fps is recommended with erosion protection. Refer

to sections 411.2 and 411.3 for protection requirements at culvert outlet.

(e)	Headwater Considerations

The maximum headwater for the 100-year design flows shall be 1.5 times the culvert

diameter, or 1.5 times the culvert rise dimension for shapes other than round. Also,

the headwater depth may be limited by the street overtopping policy in subsection

403.4(d). If the culvert outlet velocity is greater than 12 fps, an energy

dissipator shall be required. Refer to section 411.3 of these criteria.

(f)	Structural Design

As a minimum, all culverts shall be designed to withstand an HS-20 loading (unless

designated differently by the City Engineer) in accordance with the design

procedures of AASHTO, "Standard Specifications for Highway Bridges," and with the

pipe manufacturer's recommendation.

(g)	Trashracks

Trashracks may be required at the entrance of culverts for some installations as

designated by the City Engineer. Installation of trashracks prevents debris from

entering culverts. The culverts are protected from blockage since the debris

accumulates at the trashracks. This centralized collection point allows routine

cleaning of trashracks and hauling away of debris, which further protects culverts

from blockage during flood events. In the event that someone is trapped in a channel

during flood flows, a trashrack shall enable the individual to climb to safety and

not be swept into the culvert.

The following criteria shall be used for design of trashracks for storm drainage

applications:

1.	Materials

All trashracks shall be constructed with smooth steel pipe with a minimum 1.25

inches outside diameter. Smaller diameter pipe/bars may be required at the

discretion of the City Engineer. The trashracks ends and bracing should be

constructed with steel angle sections. All trashrack components shall have a

corrosion protective finish.

2.	Trashrack Design

The trashracks shall be constructed without cross-braces (if possible) in

order to minimize debris clogging. The trashrack shall be designed to withstand

the full hydraulic load of a completely plugged trashrack based on the highest

anticipated depth of ponding at the trashrack. The trashrack shall also be

hinged and removable for maintenance purposes.

3.	Bar Spacing

The steel pipe bars shall be spaced with a maximum clear opening of six inches.

In addition, the entire rack shall have a minimum clear opening area (normal to

the rack) at the design flow depth of four times the culvert opening area.

4.	Trashrack Slope

The trashrack shall have a longitudinal slope of no steeper than 2.5 horizontal

to 1 vertical for maintenance purposes.

5.	Hydraulics

Hydraulic losses through trashracks shall be computed using the following

equations:

Ht = 0.11 (TV/D2) (Sin A)          (Equation 400-10)

where  Ht = Head Loss through Trashrack (feet)

T = Thickness of Trashrack Bar (inches)

V = Velocity Normal to Trashrack (fps)

D = Center-to-Center Spacing of Bars (inches)

A = Angle of Inclination of Rack with Horizontal

The equation shall apply to all racks constructed normal to the approach flow

direction. The velocity normal to the trashrack shall be computed considering

the rack to be 50 percent plugged.

(h)	Low Water Crossing

A low water crossing is a privately constructed and maintained embankment structure

which provide property ingress and egress across a floodplain. The drainage

classification of the street is Type A (see section 409.3). The capacity of the

structure is designed to allow access across the drainageway during runoff from a

minor storm. Access generally shall not be possible during runoff from a major

storm.

1.	Design Standards

The standards for design of low water crossing are listed below.

a.    Embankment

Slopes on earthen riprapped or sloped, paved embankments shall not be

steeper than three (horizontal) to one (vertical). All earthen slopes

shall be covered with topsoil and revegetated with grass.

b.    Slope Paving and Headwall

The slope paving shall extend to the edge of the proposed roadbed. At

the designer's option, the slope paving and headwall may be replaced

by a vertical headwall with wingwalls located at the roadbed edge. The

headwall and wingwalls shall be designed as shown on CDOT standard M-

601-12 and M-601-20.

c.    Culverts

Culvert types used for a low water crossing shall be determined as per

subsection 410.3.

d.    Riprap

Riprap culvert and slope protection shall be designed as per section

411.2. The downstream riprap slope protection limits are defined in a

horizontal plane by a line drawn two (parallel) to one (perpendicular)

to the culvert centerline starting from the downstream edge of the

roadbed to the end of the culverts.

e.    Road Surface

The roadside over the crossing may be constructed of any materials

acceptable to the City Engineer.

2.	Criteria

A low water crossing shall be designed to meet the following criteria:

a.    The capacity of the crossing shall be less than the peak flow from a

minor storm with less than six-inches overtopping of the road embankment.

For low water crossing, the minor storm is defined as a storm which

produces runoff equal to the mean annual flood. The mean annual flood has

a recurrence interval of 2.33 years. The mean annual flood peaks for use

in the City shall be determined from Figure 400-36.

b.    Backwater from the low water crossing shall not increase the 100-year

water surface elevation more than one foot as defined by adopted

floodplain information report (see Section 402).

3.	Maximum Crossing Height

The crossing height for a low water crossing is defined as the distance

between the highest point on the road surface and the channel invert. The

maximum crossing height shall be determined by comparing the channel

conveyances at the crossing section with and without the proposed crossing.

The 100-year flood conveyance of the channel section with the proposed

crossing and the allowable increase in the 100-year floodplain shall be

greater than the 100-year conveyance of the channel section without the

crossing.

The procedure used for calculation of the maximum crossing height is presented

in the following design example.

4.	Culvert Sizing

The culvert sizing for a low water crossing shall be completed after the

maximum crossing height is determined. The culvert sizing shall be based upon

the criteria for the minor storm as stated in section 410.3(c). Weir flow

over the crossing is allowed up to a depth of 6-inches for the minor storm

runoff. The culverts shall be sized for a capacity equal to the minor storm

runoff minus the allowable weir overflow. The procedure used for low water

cross culvert sizing is presented in the following design example.

410.4	Design Example

Presented in this example are the procedures used and data required for hydraulic

design for a low water crossing.

Example 6:    Low Water Crossing

Given:        The channel cross section shown in Figure 400-38.

Tributary Basin Area (A)* = 2.3 square miles

100-year Water Surface Elevation* = 5410.8

100-year Peak Discharge (Q)* = 6650 cfs

Average Channel Slope (S)* = 1.6 percent

*NOTE:  This data obtained from the applicable flood information report.

Required:     Allowable embankment height and culvert size and quantities.

Solution:

Step 1:	    Develop existing cross section data by using the existing ground surface

and existing 100-year water surface.

Flow area (A) = 470 ft. wetted perimeter (WP) = 150 ft,

hydraulic radius (R) = A/WP = 470/150 = 3.13.

Step 2:       Calculate existing channel n-value for the 100-year flood

n    = 1.49 R2/3  S1/2  A/Q

= 1.49 (3.13)2/3  (.016)1/2  (470)/6650

= 0.0285

Step 3:       Calculate existing channel conveyance (K) for the 100-year flood

K    = Q/S1/2

= 6650/(0.016)1/2

= 52,600

Step 4:       Compute the net conveyance of the proposed crossing for various crossing

heights using the computed n-value and with a water surface elevation

one foot higher than the existing 100-year water surface elevation. The

crossing height is the distance from the existing channel invert to the

top of the proposed road embankment. The net conveyance is then the

conveyance between the top of the road embankment and the 100-year water

surface elevation raised by one foot.

Proposed 100-year water surface elevation = 5410.8 + 1.0 = 5411.8.

See sample conveyance calculation on Figure 400-38.

Step 5: 	    Plot channel conveyance (K) versus crossing height (H) from the date

computed in Step 4.

See sample graph on Figure 400-38.

Step 6:	    Determine the maximum allowable crossing height (H):

Using the existing conveyance (K) of 52,600, read from the graph a maximum

crossing height (H) of 3.5-feet.

Step 7:	    Determine the mean annual flood (Q2.3) at the proposed crossing location:

Using a drainage area of 2.3 square miles, read from Figure 400-367 a mean

annual flood peak discharge of 300 cfs.

Step 8:	    Determine the allowable crossing overflow (Qo) at the maximum crossing

height with a maximum overflow depth of 0.5-foot.

Using the weir equation (Qo) = CLH1.5 with C = 2.8 (use for all low water

crossing weir overflow computations) and with a weir length (L) of 76-feet,

calculated the allowable overtopping flow rate:

Qo = 2.8 (76)(0.5)1.5

Qo = 75 cfs

Step 9:	    Determine the minimum required culvert capacity (Qp)

Qp = Q2.3 - Qo

= 300 - 75

Qp 225 cfs

Step 10:	    Select culvert size

Use 58" x 36" CMPA (minimum three foot high culvert)

(3.5' - 36"/12 = 0.5' of cover)

Note:  Since this cover is less than the minimum cover recommended by the

manufacturer for H-20 loading, the traffic should be restricted or other

structural measures incorporated into the design.

Step 11:	    Calculate number of culverts required

Assuming inlet control, using an applicable design nomograph with HW/D

= 48"/36" = 1.33, the capacity of a single culvert is about 80 cfs

The number of culvert is

= 225 cfs/80 cfs per culvert

= 3 culverts

Thus, use (3) 58" by 36" CMPA culverts with a 3.5-foot high crossing.

DESIGN EXAMPLE

The procedure recommended to evaluate existing and proposed culverts is based on the

procedures presented in HEC-5 Reference-12. The methodology consists of evaluating the

culvert headwater requirements, assuming both inlet control and outlet control. The

rating that results in the larger headwater requirements is the governing flow condition.

Example 7:    Culvert Rating

A sample calculation for rating an existing culvert is presented in figure 400-37. The

required data are as follows:

Culvert size, length, and type (48" CMP, L = 150', n = .024).

Inlet, outlet elevation, and slope (5540.0, 5535.5, So = 0.030).

Inlet treatment (flared-end section).

Low point elevation of embankment (EL = 5551.9).

Tailwater rating curve (see Figure 400-3, Column 5).

From the above data, the entrance loss coefficient, K2, and the n-value are determined.

The full flow Q and the velocity are calculated for comparison. The rating proceeds in

the following sequence:

Step 1:	Headwater values are selected and entered in column 3. The headwater to pipe

diameter ratio (Hw/D) is calculated and entered in column 2. If the culvert

is other than circular, the height of the culvert is used.

Step 2:	For the Hw/D ratios, the culvert is read from the rating curves (section

410.3(c) and entered into column 1. This completes the inlet condition rating.

Step 3:	For outlet condition, the Q values in column 1 are used to determine the head

values (H) in column 4 from the appropriate outlet rating curves (section

410.3(c).

Step 4:	The tailwater depths (Tw) are entered into column 5 for the corresponding Q

values in column 1 according to the tailwater rating curve (i.e., downstream

channel rating computations). If a tailwater rating curve is not available,

then the tailwater can be approximated by calculating the normal depth for each

flow value using the trapezoidal section (noted on Figure 400-37). If the

tailwater depth (Tw) is less than the diameter of the culvert (D), columns 6

and 7 are to be calculated (go to Step 5). If Tw is more than D, the tailwater

values in column 5 are entered into column 8 for the (ho) values, and proceed

to Step 6.

Step 5:	The critical depth (dc) for the corresponding Q values in column 1 are entered

into column 6. The average of the critical depth and the culvert diameter is

calculated and entered into column 7 and the (ho) values.

Step 6:	The headwater values (Hw) are calculated according to the equation.

Hw = H + ho - LSo

where H is from column 4, and (ho) is from column 8 (for Tw>D) or the larger

value between column 5 and column (for Tw<D). The values are entered into

column 9.

Step 7:	The final step is to compare the headwater requirements (columns 9 and 3) and

to record the higher of the two values in column 10. The type of control is

recorded in column 11, depending upon which case gives the higher headwater

requirements. The headwater elevation is calculated by adding the controlling

Hw (column 10) to the upstream invert elevation. A culvert rating curve can

then be plotted from the values in columns 12 and 1.

To size a culvert crossing, the same form can be used with some variations in the

basic procedures. First, a design capacity is selected and the maximum allowable

headwater is determined. An inlet type (i.e., headwall) is selected, and the invert

elevations and culvert slope are estimated based upon site constraints. A culvert type

is then selected and first rated for inlet control and then for outlet control. If the

controlling headwater exceeds the maximum allowable headwater, a different culvert

configuration is selected and the procedure repeated until the desired results are

achieved.

410.5	Culvert Sizing Criteria

The sizing of a culvert is dependent upon two factors, the drainage classification

(i.e., Type-A, Type-B, or Type-C) and the allowable street overtopping. The allowable

street overtopping for the various street classifications is set forth in subsection

403.4(d). In addition to this policy, a criteria requiring that no street overtopping

occur for a 10-year frequency storm has been established. Therefore, as a minimum

design standard for street crossing, the following procedure shall be used:

1.	Using the future developed conditions 100-year runoff, the allowable street

overtopping shall be determined from overflow rating curves developed from the

street profile crossing the waterway.

2.	The culvert is then sized for the difference between the 100-year runoff the

allowable overtopping.

3.	If the resulting culvert is smaller than required to pass the 10-year flood peak

without overtopping, the culvert shall be increased in size to pass the 10-year

flow.

The criteria is considered a minimum design standard and must be modified where other

factors are considered more important. For instance, if the procedure still results in

certain structures remaining in the 100-year floodplain, the design frequency may be

increased to lower the floodplain elevation. Also, if only a small increase in culvert

size is required to prevent overtopping, then the larger culvert is recommended.

410.6	Checklist

To aid the designer and reviewer, the following checklist has been prepared:

(1)	Minimum culvert size within the public ROW is 24-inch diameter round or equivalent

for other shapes.

(2)	Minimum culvert size for roadside ditches at driveways in 18-inch diameter round

or equivalent for other shapes.

(3)	Headwalls, wingwalls, or flared-end sections required for all culverts.

(4)	Check outlet velocity and provide adequate protection.

(5)	Check maximum headwater for design condition.

(6)	Check structural requirements.

411	HYDRAULIC STRUCTURES

411.1	Erosion Control

Hydraulic structures are used in storm drainage work to control the flow of the runoff.

The energy associated with flowing water has the potential to create damage to the

drainage works, especially in the form of erosion. Hydraulic structures, which include

riprap, energy dissipators, check structures, bridges, and irrigation ditch crossings,

all control the energy and minimize the damage potential of storm runoff.

The criteria to be used in the design of hydraulic structures shall be in accordance with

the UD&FCD Manual Volume 2 in the "Major Drainage" and "Structures" sections. The

specific criteria to be used with the modifications for the county are presented herein.

411.2	Riprap

The design of the riprap protection for culverts, channel bottom and banks, check drops,

bridges, gabions or other areas subject to erosion, shall be in accordance with the

UD&FCD Manual Volume 2, "Major Drainage Section 5 - Riprap," as revised.

411.3	Energy Dissipators

Where riprap structures are insufficient or uneconomical to control the storm runoff,

concrete energy dissipator structures (stilling basins) shall be provided in accordance

with the UD&FCD Manual Volume 2 "Structures, Section 2.2 - Energy Dissipators."

For culverts or storm sewers where the Froude number at the outlet is in excess of 2.5,

the USBR Type VI impact stilling basin shall be used. An example USBR Type VI basin is

shown in Figure 400-39.

411.4	Check Structures

As discussed in chapter, "Open Channels," there is a maximum permissible velocity for

major design storm runoff in grass lined channels. One of the more common methods of

controlling the flow velocity is to reduce the channel invert slope, which requires

a check drop to make up for the elevation difference occurring when the channel slope

is reduced.

The design criteria for the check drops shall be in accordance with the UD&FCD Manual

Volume 2 "Structures, Section 3 - Channel Drops." This section is being redrafted by the

Urban Drainage and Flood Control District. Draft copies of the preliminary work may be

obtained from the Urban Drainage and Flood Control District.

411.5	Bridges

The design of bridges within the City shall be in accordance with the UD&FCD Manual

Volume 2, "Structures, Section 4 - Bridges." The design capacity of the bridge shall

be determined by the method presented in section 410.5 of these criteria.

411.6	Irrigation Ditch Crossings

The City is traversed by several irrigation ditches and canals. Any development that is

traversed by one of these ditches or canals shall have the approval of the ditch

company to cross their facility either over or under prior to submittal for approval by

the City Engineer.

412	CONTROL OF EROSION AND SEDIMENTATION FROM CONSTRUCTION

412.1	Introduction

All site development applications shall include an erosion and sedimentation plan (refer

to subsection 403.3(h)). The plan shall be prepared and shall be reviewed in accordance

with the criteria presented in this subsection.

The clearing and stripping of land for development can cause high localized erosion

rates with subsequent deposition and damage to off-site properties. Whereas erosion and

sedimentation is a natural process, the intensity is increased by development which can

destroy the aesthetic and practical values of other properties, streams, and lakes. The

purpose of this section is to prevent soil erosion and sedimentation from leaving

construction sites that occur from non-agricultural development and construction

activities within the City, by requiring proper provisions for water disposal and the

protection of soil surfaces during and after construction, in order to promote the

safety, public health, convenience and general welfare of the community.

A permit shall be obtained in accordance with City ordinance in order to prevent soil

erosion and sedimentation from leaving construction sites. Any person who undertakes

or is responsible for an undertaking which involves earth disturbance is ultimately

responsible to see that soil erosion and sedimentation as well as changed water flow

characteristics resulting therefrom are controlled to the extent necessary to avoid

damage to property and to avoid pollution of receiving waters. The standards, criteria

and requirements of this subsection are to be seen as minimum standards which are not

necessarily adequate to meet the highly variable conditions which must be covered by

effective control measures. Compliance with the requirements of this subsection may not,

therefore, of itself discharge such person's responsibility to provide effective control

measures.

Subsequent to the passage of the Federal Water Pollution Control Act Amendments (PL-

92-500), the Denver Regional Council of Government (DRCOG) initiated a federally

funded area-wide water quality management study. The result of the study ("Clean

Water Plan") identified the control of pollutants which originate from non-point or

diffuse sources as an important consideration requiring preventative measures for

developing areas. A manual of best management practices for erosion and sedimentation

control was prepared by DRCOG to define, explain, and guide the protection of land and

water resources within the Denver metropolitan area. The information and guidelines

presented herein, utilize the DRCOG best management practices manual as well as

subsequent publications of DRCOG.

The erosion control plan is required at the time of drainage study submittal since the

site grading is often the first step in construction and final plans for streets and

storm sewer may not be available at that time. The erosion control plan can be submitted

on separate 24 inches x 36 inches drawings so it can be incorporated into the

construction plans at a later date. Because erosion control plan approval is necessary

for issuance of the City overlot grading permit, the Responsible Party typically wants

this approval at the earliest possible time. The earliest appropriate time for submitting

the erosion control plan is with the Phase-II Drainage Report.

412.2	Standards and Requirements

(a)	Guidelines

1.	"Managing Erosion and Sedimentation from Construction Activities," DRCOG,

2480 West 26th Avenue, Suite 200-B, Denver, Colorado 80211, April 1980.

2.	"Factors Affecting the Cost of Erosion Control Planning," DRCOG, 2480 West

26th Avenue, Suite 200-B, Denver, Colorado 80211, June 1982.

3.	"Cost of Erosion Control Measures," DRCOG, 2480 West 26th Avenue, Suite

200-B, Denver, Colorado 80211, May 1982.

(b)	Planning Submittals

1.	Requirements

All subdivision, zoning and any other proposed development plans submitted

for approval shall include adequate erosion and storm water pollution control

design, management, and maintenance arrangements before approval of any phase

of the construction shall be made. Such design shall reflect the purposes and

criteria presented herein and in the adopted guidelines (refer to section

412.2(a).

Five elements of an erosion control plan have been identified by DRCOG as

follows:

1.    Gather information on topography, soils, drainage, vegetation, and

other site features.

2.    Analyze the information in order to project the magnitude of erosion

and sedimentation.

3.    Devise a plan which schedules construction activities, thereby

minimizing the potential for serious erosion/sedimentation.

4.    Develop an erosion control plan which specifies effective erosion/

sedimentation control measures.

5.    Follow the erosion control plan, and revise it when necessary.

All or portions of the above elements may be required during the development

process. The elements required are illustrated by Figure 400-40. As a minimum,

elements 1 and 2 shall be required along with the platting process. At this

time, the plan shall be reviewed to determine if a final plan and the

associated construction details are required. The decision as to the necessity

for a final plan shall be based on project size, amount of grading, soil type,

slopes of the site, and proximity to areas likely to be damaged by erosion and

sedimentation. The criteria for evaluation are set forth in the table below:

TABLE 400-10

CRITERIA FOR FINAL EROSION CONTROL AND SUBMITTAL

Control                          Submittal of Plan Required

Land Slope>18%                             Yes

Soil Erodibility Factor (K)>0.37           Yes

Land Slope>6% and K>0.24                   Yes

Site<500' from a Water Course              Yes

Unsheltered Distance>500'                  Yes

Impervious Area>10,000 sq. ft.             Yes

Any combination of the above               Yes

2.	Reporting

Since erosion control planning is an extension of the grading and drainage

planning process, the erosion control planning is not an entirely independent

process. The drainage reporting outlined in Section 402 of this manual shall

include a section dealing with erosion control planning (as required) and

include the following additional information. Note that the amount of

information required shall depend on the stage of the development process

(refer to Figure 400-40).

Element No. 1: Information Collection

A.    Vicinity Map

B.    Topographic Map

C.    Soils Survey               - SCS survey or survey by soils scientist

D.    Vegetation Survey          - On site

E.    Climatic Data              - Precipitation and wind direction

F.    Legal Requirements

Element No. 2: Analyze Information

A.    Combine topographic, soils, and vegetation information on a map to

indicate critical areas. This forms the basis for the site analysis

drawing. Preliminary site layout should then be added to map.

B.    Analyze potential impact of erosion on adjacent properties.

C.    Indicate points of runoff outfall from site.

D.    Indicate (generally) how site shall be protected from erosion.

E.    Meet with local government to decide whether a comprehensive erosion

control plan is necessary.

If a comprehensive erosion control plan is needed, continue to Element 3.

Element No. 3: Prepare a Site Development Plan

A.    Consider modification to the preliminary site layout in order to make

the best fit between the site's natural characteristics and the proposed

land use to minimize earth change and disturbance of critical areas.

B.    Illustrate how runoff volume and velocity shall be accommodated.

C.    Illustrate how wind velocity shall be accommodated.

Element No. 4: Prepare Final Erosion Control Plan

A.    Obtain (develop) drainage plan. This is the starting point for the

erosion control plan.

B.    Prepare final erosion control plan.

1.    Stage construction (yearly schedule).

2.    Schedule all earth change activities (bar schedule).

3.    Locate all temporary erosion and sedimentation control facilities.

4.    Locate all permanent erosion and sedimentation control facilities.

Those items which are not included in the drainage plan shall

already be shown; the manner in which drainage-related

appurtenances mitigate erosion should be noted.

C.    Certification of the Erosion Control Plan by the owner's engineer for

compliance with the criteria is required. The certification sheet shall

be stated as follows:

"I hereby certify that this Erosion Control Plan for          Name of

Development      was prepared by me (or under my direct supervision in

accordance with the provisions of the City of Scottsbluff Storm Drainage

Design and Technical Criteria for the owners thereof."

Registered Professional Engineer

State of Nebraska No.

(Affix Seal)

(According to the State of Nebraska Board of Registration, the plan or

certification sheet should not be a mylar or reproducible sheet.

(c)	Performance Standards

The general requirements for erosion control work shall be as follows:

1.	All temporary erosion control facilities and all permanent facilities intended

to control erosion of any earth disturbance operation shall be installed before

any earth disturbance operations take place.

2.	Any earth disturbances shall be conducted in such a manner so as to effectively

reduce accelerated soil erosion and resulting sedimentation, and should not

exceed the erosion expected to occur for the site in its totally undeveloped

state.

3.	All persons engaged in earth disturbances shall design, implement, and

maintain acceptable soil erosion and sedimentation control measures, in

conformance with the erosion control technical standards adopted by the City.

4.	All earth disturbances shall be designed, constructed and completed in such a

manner so that the exposed area of any disturbed land shall be limited to the

shortest possible period of time.

5.	Sediment caused by accelerated soil erosion shall be removed from runoff water

before it leaves the site of the earth disturbance.

6.	Any temporary or permanent facility designed and constructed for the conveyance

of water around, through, or from the earth disturbance area shall be designed

to limit the water flow to a non-erosive velocity.

7.	Temporary soil erosion control facilities shall be removed and earth

disturbance areas graded and stabilized with permanent soil erosion control

measures pursuant to Standards and Specifications prescribed in accordance

with the provisions of the "Erosion and Sediment Control for Construction

Activities" and in accordance with the permanent erosion control features

shown on the soil stabilization plan approved by the City.

8.	Permanent soil erosion control measures for all slopes, channels, ditches, or

any disturbed land area shall be completed within 14 calendar days after final

grading or the final earth disturbance has been completed. When it is not

possible to permanently stabilize a disturbed area after an earth disturbance

has been completed or where significant earth disturbance activity ceases,

temporary soil erosion control measures shall be implemented within 14

calendar days. All temporary soil erosion control measures shall be maintained

until permanent soil erosion measures are implemented.

(d)	Overlot Grading Permits and Construction Observation

Before construction begins, the applicant shall apply for an Overlot Grading

Permit to the City Engineer. A permit shall be issued if an Erosion Control Plan

has been submitted and approved.

The City Engineer shall monitor all overlot grading activities for compliance with

the Overlot Grading Permit. If the construction activities are not in compliance

with the intent of the Erosion Control Plan, the Responsible Party shall be issued

a stop-work order.

(e)	Minimum Design Standards for Erosion and Sediment Control

All erosion control plans and specifications including extension of previously

approved plans shall include provisions for erosion and sediment control in

accordance with the "Erosion and Sediment Control for Construction Activities".

Erosion control plans are required on sites which are:

1.	Five acres in size or larger, and all sites smaller than five acres if they

are a part of a total development or subdivision that is larger than five

acres in size; or

2.	Any development containing 15 dwelling units; or

3.	Where physical features have a cumulative effect and will create erosion

problems such as:

(a)    Steep slopes eight feet (horizontal) to one foot (vertical) or steeper,

and

(b)    Significantly erodible soils - "K" in the universal soil loss equation

is greater than or equal to 0.25;

(f)	Variances and Exceptions

Exemptions from the erosion control process may be granted by the City Engineer for

the following conditions:

1.	Agricultural use or land zoned agricultural.

2.	Grading or an excavation below finished grade for basements, footings,

retaining walls, or other structures on plots zoned R1-R3 of less than five

acres in size unless required otherwise.

3.	A sidewalk or driveway authorized by a valid permit.

4.	Gravel, sand, dirt or topsoil removal as authorized pursuant to approval of

the Nebraska Mined Land Reclamation Board, provided said approval includes

an erosion plan that meets the minimums specified by this ordinance.

5.	Sites smaller than five acres which are not a part of a larger development and

which constitute an infill of an established older development within the City.

6.	Where the City Engineer certifies in writing that the planned work and the

final structures or topographical changes will not result in or contribute to

soil erosion or sedimentation and will not interfere with any existing drainage

course in such a manner as to cause damage to any adjacent property or result

in the deposition of debris or sediment on any public way, will not present

any hazard to any persons or property, and will have no detrimental influence

upon the public welfare or upon the total development of the watershed.

7.	Even though no permits are required under subsection 412.2(b) of this section,

those operations and construction activities which are exempted from obtaining

permits must comply with the rules and regulations concerning grading and

erosion specified in this section, and shall provide appropriate controls to

retain soil erosion on the construction site.

(g)	Modifications of Approved Plans

All proposed modifications of the approved grading plan must be submitted along

with all supporting materials to the City Engineer. No work in connection with the

proposed modifications shall be permitted without prior approval of the City

Engineer, approval for which may be issued if the applicant can demonstrate that

the modifications will provide soil erosion controls equivalent to, or better than

the originally approved soil disturbance plans.

(h)	Maintenance Requirements

Persons carrying out soil erosion and sediment control measures under this section,

and all subsequent owners of property concerning which such measures have been

taken, shall maintain all permanent erosion control measures, retaining wall,

structures, plantings and other protective devices. Should the applicant or any of

the subsequent property owners fail to adequately maintain the permanent erosion

control facilities, retaining walls, structures, plantings and other protective

devices; the City reserves the authority, after properly notifying the owner of

needed maintenance and the owner failing to respond to the City's demand for such

maintenance, to enter affected property, provide needed maintenance and to charge

the owner for the work performed by the City or its contractors.

413	DETENTION

413.1	Introduction

The criteria presented in this subsection shall be used in the design and evaluation of

all detention facilities. The review of all planning submittals (refer to section 402)

shall be based on the criteria presented in this subsection.

The main purpose of a detention facility is to store the excess storm runoff associated

with an increased basin imperviousness and discharge this excess at a rate similar to

the rate experienced from the basin without development. The value of such detention

facilities is discussed in subsection 403.3(f). Any special design conditions which

cannot be defined by these criteria shall be reviewed by the City Engineer before

proceeding with design.

413.2	Detention Methods

The various detention methods are defined on the basis of where the facility is

constructed, such as open space detention, parking lot, or underground.

413.3	Design Criteria

(a)	Volume and Release Rates

The minimum required volume shall be determined using the CUHP method or the

following equations. These empirical equations were developed as part of the

UD&FCD hydrology research program. The equations are based on a computer modeling

study and represent average conditions. One of the most difficult aspects of

storm drainage is obtaining consistent results between various methods for

estimating detention requirements. These equations shall provide consistent and

more effective approaches to the sizing of on-site detention ponds. For larger

water sheds where the Colorado Urban Hydrograph Procedure CUHP can be used, (i.e.,

+/- 90 acres), hydrograph routing procedures shall be permitted in the design of

these ponds, provided the historic imperviousness of two percent or less is used.

Minimum Detention Volume:

V = KA	(Equation 400-11)

For the 100-year,

K100 = (1.78I - 0.0021/2 - 3.56)/1000    (Equation 400-12)

For the 10-year,

K10 = (0.95I - 1.90)/1000	(Equation 400-13)

Where V = required volume for the 100- or 10-year storm (acre feet)

I = Developed basin imperviousness (%)

A = Tributary area (Acres)

The maximum release rates at the ponding depths corresponding to the 10- and

100-year volumes are as follows:

TABLE 400-11

ALLOWABLE RELEASE RATES FOR DETENTION PONDS - CRS/ACRE

SOIL GROUP

CONTROL FREQUENCY       A     B     C & D

10-Year                0.13  0.23    0.30

100-Year               0.50  0.85    1.00

The predominate soil group for the total basin area tributary to the detention pond

shall be used for determining the allowable release rate.

(b)	Design Frequency

All detention facilities are to be designed for two storm frequencies: the 10-year

and the 100-year recurrence interval floods (see subsection 403.3(f)).

(c)	Hydraulic Design

Hydraulic design data for sizing of detention facilities outlet works is as follows:

1.	Weir Flow

The general form of the equation for horizontal crested weirs is:

Q = CLH3/2	(Equation 400-14)

Where  Q = discharge (cfs)

C = weir coefficient    (Figure 400-41)

L = horizontal length (feet)

H = total energy head (feet)

Another common weir is the v-notch, whose equation is as follows:

Q = 2.5 tan (O/2)H5/2	(Equation 400-15)

Where  O = angle of the notch at the apex (degrees)

When designing or evaluating weir flow, the effects of submergence must be

considered. A single check on submergence can be made by comparing the

tailwater to the headwater depth. The example calculation for a weir design

on Figure 400-44 illustrates the submergence check.

2.	Orifice Flow

The equation governing the orifice opening and plate is the orifice flow

equation:

Qd = Cd A (2gh)1/2      (Equation 400-16)

Where  Q - Flow (cfs)

Cd - Orifice coefficient

A = Area (ft2)

g = Gravitational constant = 32.2 ft/sec2

h = Head on orifice measured from centerline of orifice

An orifice coefficient (C sub d) value of 0.65 shall be used for sizing of

square edged orifice openings and plates.

413.3	Design Standards for Open Space Detention

(a)	State Engineer's Office

Any dam constructed for the purpose of storing water, with a surface area, volume,

or dam height as specified in Colorado Revised Statutes 37-87-105 as amended,

shall require the approval of the plans by the State Engineer's Office. All

detention storage areas shall be designed and constructed in accordance with these

criteria. Those facilities subject to state statutes shall be designed and

constructed in accordance with the criteria of the state.

(b)	Grading Requirements

Slopes on earthen embankments less than five feet in height shall not be steeper

than four (horizontal) to one (vertical). For embankment heights between five

feet and 10 feet, the slopes shall not be steeper than three (horizontal) and 1

(vertical), but horizontal slope distance shall not be less than 20 feet. For

embankments greater than 10 feet in height, the slopes shall be such to maintain

slope stability, but horizontal slope distance shall not be less than 30 feet.

Contact the City Engineer for additional requirements. All earthen slopes shall

be covered with topsoil and revegetated with grass. Slopes on riprapped earthen

embankments shall not be steeper than three (horizontal) to one (vertical). For

grassed detention facilities, the minimum bottom slope shall be 0.5 percent

measured perpendicular to the trickle channel.

(c)	Freeboard Requirements

The minimum required freeboard for open space detention facilities is one foot

above the computed 100-year water surface elevation.

(d)	Trickle Flow Control

All grassed bottom detention ponds shall include a concrete trickle channel or

equivalent performing materials and design. Trickle flow criteria is presented in

section 406.4(b).

(e)	Outlet Configuration

Presented on Figure 400-42 are two examples for detention pond outlet configuration.

A Type I outlet consists of a grated drop inlet, outlet pipe, and an overflow weir

in the pond embankment. The control for the 10-year discharge shall be at the throat

of the outlet pipe under the head of water as defined on Figure 400-42. The grate

must be designed to pass the 10-year flow with a minimum of 50 percent blockage,

(i.e., twice the 10-year flow). Since the minimum size of the outlet pipe is 12-

inches, then a control orifice plate at the entrance of the pipe may be required

to control the discharge of the design flow. An example orifice plate is shown on

Figure 400-43. Other outlet configurations shall be allowed provided they meet the

requirements of the permitted release rates at the required volume and include

proper provisions for maintenance and reliability.

The outlet shall be designed to minimize unauthorized modifications which effect

proper function. A sign with a minimum area of 0.75 square feet shall be attached

to the outlet or posted nearby with the following message:

"WARNING

Unauthorized modification of this outlet is a code

violation and subject to the penalties of the Code."

The difference between the 100-year discharge and the surcharged discharge on

the 10-year outlet is released by the overflow weir or spillway. If sufficient

pond depth is available, the drop inlet and the grate can be replaced by a

depressed inlet with a headwall and trashrack. Depression of the inlet is required

to reduce nuisance backup of flow into the pond during trickle flows. The maximum

trashrack opening dimension shall be equal to the minimum opening in the orifice

plate.

A Type 2 outlet consists of a drop inlet with an orifice controlled for the 10-year

discharge and a crest overflow and pipe inlet control for the 100-year discharge.

However, the difference between the 100-year and 10-year discharge must pass over

the weir and therefore the weir must be of adequate length. The effective weir

length (L) occurs for three sides of the box. To ensure the 100-year control

occurs at the throat of the outlet pipe, a 50 percent increase in the required

weir length is recommended. In addition, the outlet pipe must have an adequate

slope to ensure throat control in the pipe.

(f)	Embankment Protection

Whenever a detention pond uses an embankment to contain water, the embankment

shall be protected from catastrophic failure due to overtopping. Overtopping can

occur when the pond outlets become obstructed or when a larger than 100-year

storm occurs. Failure protection for the embankment may be provided in the form

of a buried heavy riprap layer on the entire downstream face of the embankment or

a separate emergency spillway having a minimum capacity of twice the maximum release

rate for the 100-year storm. Structures shall not be permitted in the path of the

emergency spillway or overflow. The invert of the emergency spillway should be set

equal to or above the 100-year water surface elevation.

(g)	Vegetation Requirements

All open space detention ponds shall be revegetated by either irrigated sod or

natural dry-land grasses as required in Section 800 of these Standards and

Specifications.

413.5	Design Standards for Parking Lot Detention

The requirements for parking lot detention are as follows:

(a)	Depth Limitation

The maximum allowable design depth of the ponding for the 100-year flood is nine

inches.

(b)	Outlet Configuration

The minimum pipe size for the outlet is 12 inch diameter where a drop inlet is used

to discharge to a storm sewer or drainageway. Where a weir and a small diameter

outlet through a curb are used, the size and shape are dependent on the discharge/

storage requirements. A minimum pipe size of three inch diameter is recommended.

Discharge across a walk or in an upstream direction from the street gutter flow is

not permitted.

(c)	Performance

To assure that the detention facility performs as designed, maintenance access shall

be provided in accordance with subsection 403.3(g). The outlet shall be designed to

minimize unauthorized modifications which effect the function. Any repaving of the

parking lot shall be evaluated for impact on volume and release rates and are

subject to approval by the City Engineer prior to issuance. Detention within a

parking lot which inundates the entrance or exit areas of a building shall not be

permitted. Detention on public rights-of-way shall not be permitted. Sanitary

sewer manholes shall not be permitted within the detention area. A sign shall be

attached or posted in accordance with subsection 413.4(e).

(d)	Flood Hazard Warning

All parking lot detention areas shall have a minimum of two signs posted identifying

the detention pond area. The signs shall have a minimum area of 1.5 square feet and

contain the following message:

"WARNING

This area is a detention pond and is subject to periodic flooding to

a depth of (provide design depth for 10-year or 100-year storm,

whichever shall be contained in parking lot)."

Any suitable weather resistant material and geometry of the sign are permissible,

subject to approval by the City Engineer.

413.6	Design Standards for Underground Detention

The requirements for underground detention are as follows:

(a)	Materials

Underground detention shall be constructed using corrugated aluminum pipe (CAP)

or reinforced concrete pipe (RCP). The pipe thickness cover, bedding, and backfill

shall be designed to withstand HS-20 loading for parking or as required by the

City.

(b)	Configuration

Pipe segments shall be sufficient in number, diameter, and length to provide the

required minimum storage volume for the 100-year design. As an option, the 10-

year design can be stored in the pipe segments and the difference for the 100-year

stored above the pipe in an open space detention (subsection 413.4) or in a

parking lot detention (subsection 413.5). The minimum diameter of the pipe segments

shall be 36-inches.

The pipe segments shall be placed side by side and connected at both ends by elbow

tee fittings and across the fitting at the outlet (see Figure 400-45). The pipe

segments shall be continuously sloped at a minimum of 0.25 percent to the outlet.

Manholes for maintenance access (see subsection 413.6(d) shall be placed in the

tee fittings and in the straight segments of the pipe, when required.

Permanent buildings or structures shall not be placed directly above the underground

detention.

(c)	Inlet and Outlet Design

The outlet from the detention shall consist of a short (maximum 25 ft.) length(s)

of CAP or RCP with a 12 inch minimum diameter. A two-pipe outlet may be required

to control both design frequencies. The invert of the lowest outlet pipe shall

be set at the lowest point in the detention pipes. The outlet pipe(s) shall

discharge into a standard manhole or into a drainageway with erosion protection

provided per subsections 410.3(b), 411.2 and 411.3. If an orifice plate is

required to control the release rates, the plate(s) shall be hinged to open into

the detention pipes to facilitate back flushing of the outlet pipe(s).

Inlet to the detention pipes can be by way of surface inlets and/or by a local

private storm sewer system.

(d)	Maintenance Access

Access easements to the detention site shall be provided in accordance with

subsection 403.3(g). To facilitate cleaning of the pipe segments, three-foot

diameter maintenance access ports shall be placed according to the following

schedule:

TABLE 400-12

MAINTENANCE ACCESS REQUIREMENTS

Detention       Maximum            Minimum

Pipe Size       Spacing            Frequency

36" to 54"      150'               Every pipe segment

60" to 66"      200'               Every other pipe segment

>66"            200'               One at each end of the battery of pipes

The manholes shall be constructed in accordance with the detail on Figure 400-45.

413.7	Design Examples

Example 8:  Detention Design

Given:          A basin that has the following characteristics:

Basin Area (A) = 23 acres

Basin Imperviousness (I) = 55%

Predominate Soil Group = D

Required:       100-year and 10-year storage volumes and release rates.

Solution:

Step 1:  Determine K100 using Equation 400-12

K100     = (1.78I - 0.002I2 - 3.56)/1000

= (1.78(55) - 0.002(55)2 - 3.65)/1000

= 0.0883

Step 2:  Determine K10 using Equation 400-13

K10     = (0.95I - 1.90)/1000

= 0.0504

Step 3:  Determine minimum required 100-year storage volume using Equation 400-11.

V        = KA

= 0.0883 x 23

= 2.03 acre-feet (88,500 ft)3

Step 4:  Repeat Step 3 for 10-year storage

V        = KA

= 0.050 x 23

= 1.16 acre-feet (50,000 ft)3

Step 5:  Determine maximum allowed 100-year release rate

Q100     = 1.00 A

= 1.00 x 23

= 23.0 cfs

Step 6:  Repeat Step 5 for 10-year release rate

Q10      = 0.30 A

= 0.30 x 23

= 6.9 cfs

Example 9:  Detention Outlet Structure Design

Given:            Detention pond with the following characteristics (see Example 8)

Maximum 100-year release rate = 23.0 cfs

Maximum 10-year release rate = 6.9 cfs

Type 2 outlet (refer to Figure 400-45)

100-year water surface elevation = 105.0

10-year water surface elevation = 103.0

100-year outlet pipe invert elevation = 98.0

10-year outlet orifice invert elevation = 100.0

18-inch diameter outlet pipe

Required:         10-year and 100-year outlet sizing

Solution:         (see Figure 400-46)

Step 1:  Determine 10-year orifice opening size, depth to centerline of orifice =

2.5 feet.

A = Q/(Cd [2gh]1/2)    (Rearranged Equation 400-16)

= 6.9/(0.65[2(32.2)(2.5)]1/2)

= 0.84 ft2

Step 2:  Determine 10-year orifice diameter

Diameter = [4A]1/2

[n ]

= [4(.84)]1/2

[  n   ]

= 1.0 feet (12-inches)

Therefore, an orifice opening with a 12-inch diameter hole is required at

the entrance to the outlet box.

Step 3:  Determine discharge through 10-year outlet for 100-year headwater (h =

4.5 feet).

Q        = CdA (2gh)1/2    (Equation 400-16)

= 0.65(.84) [2(32.2)(4.5)]1/2

= 9.3 cfs

Step 4:  Determine discharge for sizing of 100-year weir

Qweir    = Q100 - Q (from Step 3)

= 23.0 - 9.3

= 13.7 cfs (for sizing weir only)

Step 5:  Size weir plate for 100-year outlet (18 inch RCP, h = 6.25 feet)

A        = Q/[Cd (2gh)1/2]    (Equation 400-16)

= 23.0/(0.65)[2(32.2)(6.25)])1/2

A        = 1.76 ft.2

Step 6:  Determine 100-year orifice diameter

Diameter = [4A]1/2

[n ]

= [4(1.76)]1/2

[   n   ]

= 1.5 feet = 18 inches

Since orifice diameter is approximately equal to the pipe diameter (+/- 15

percent), then no orifice plate is required.

Step 7:  Determine minimum box dimensions (i.e., weir length) to assure control of

the pipe inlet.

L = Qweir/(CH3/2)

C = 3.4 from Figure 400-41

L = 13.7/[3.4(2.0)3/2]

L = 1.4 feet

Since required weir length is only 1.4 feet, selected box dimensions suit

construction and maintenance access. A minimum size of 3' x 3' is

recommended.

Step 8:  Check minimum size for trashrack opening area

Min. area = 2 x orifice area

= (2)(1.76)

Min. area = 3.5 ft.2

Since box opening is 3 x 3 = 9 sq. ft., then design requirements are

satisfied.

413.8	Checklist

To aid the designer and reviewer, the following checklist has been prepared:

1.	Earth slopes are to be 4:1 or flatter.

2.	Minimum freeboard of 1 foot for the 100-year detention is required.

3.	Open space detention areas to include trickle channels.

4.	Protect embankment for overtopping condition by adding riprap.

5.	Provide trashracks at all outlet structures.

6.	Provide signs as required.

7.	Provide maintenance access.

SECTION 500

STREET PARKING

FACILITIES CONSTRUCTION

SECTION 500 - STREET AND PARKING FACILITIES CONSTRUCTION

TABLE OF CONTENTS			PAGE

501	GENERAL PROVISIONS		500-1

501.1	Applicability		500-1

501.2	Private Street Systems and Parking Lots	500-1

501.3	Pavement Thickness Design and Technical Criteria	500-1

502	MINIMUM DESIGN CRITERIA		500-2

502.1	Geometric Cross Section		500-2

502.2	Half Street		500-2

502.3	Horizontal Alignment		500-3

502.4	Vertical Alignment		500-3

502.5	Cul-de-Sacs		500-3

502.6	Major Structures		500-3

502.7	Design Element Coordination		500-3

502.8	Requirements of Other Jurisdictions		500-4

503	EXCAVATION AND EMBANKMENT		500-4

503.1	General			500-4

503.2	Clearing and Grubbing		500-4

503.3	Removal of Miscellaneous Materials		500-5

503.4	Protection of Utility Lines and Structures	500-6

503.5	Protection of Public and Private Installations	500-7

503.6	Excavation and Embankment		500-7

503.7	Borrow			500-8

503.8	Subgrade			500-8

503.9	Subbase Construction		500-8

504	BITUMINOUS CONSTRUCTION		500-10

504.1	General			500-10

504.2	Base Course		500-10

504.3	Hot Bituminous Pavement		500-11

504.4	Tack Coat			500-13

504.5	Seal Coat			500-13

504.6	Rejuvenating Agent		500-14

504.7	Heating and Scarifying		500-14

504.8	Grinding			500-14

505	CONCRETE PAVEMENT		500-15

505.1	Portland Cement Concrete Pavement		500-16

505.2	Aggregate Base Course Material		500-16

505.3	Subgrade Investigation and Pavement Design Report	500-16

506	APPURTENANT CONCRETE STRUCTURES		500-16

506.1	General			500-16

506.2	Materials			500-17

506.3	General Requirements		500-17

506.4	Construction Requirements		500-18

507	INSPECTION				500-21

507.1	General			500-21

507.2	Required Inspection		500-21

507.3	Required Testing		500-22

507.4	Utility Installation		500-22

507.5	Street Lighting		500-22

508	ROADWAY INSPECTION AND TESTING		500-22

508.1	General			500-22

508.2	Inside Rights-of-Way		500-22

508.3	Test Listing		500-22

508.4	Roadway Subgrade Preparation		500-23

508.5	Lime Treated Subgrade		500-24

508.6	Aggregate Base Course		500-24

508.7	Plant Mix Bituminous Pavements		500-25

508.8	Portland Cement Concrete		500-26

508.9	Asphalt Prime and Tack Coats		500-27

508.10	Geotextile Fabric		500-28

TABLES

500-1	Material Specifications for Hot Bituminous Pavement	500-12

500-2	Mix Tolerances		500-13

500-3	Mix Design Criteria for Asphalt Concrete	500-13

500-4 	Moisture-Density Control		500-23

DETAIL DRAWINGS

500-1	Typical Street Cross Sections

500-2	Typical Street Cross Sections

500-3	Typical Section Alley

500-3A	Typical Section

500-4	Typical Right In - Right Out Access Standard Arterial Roadway

500-5	Sight Distance

500-8	Type 1 and 2 Curb and Gutter

500-10	Squared Radius With Cross Pan Industrial/Arterial/Collector Street

500-11	Squared Radius With Cross Pan Local Service Street

500-12	Type L-1 Sidewalk Ramp Local Service Street

500-13	Type C-1 Sidewalk Ramp Collector Street

500-14	Type A-2 Sidewalk Ramp Arterial Street

500-15	Driveway Apron Detail Local Service Street

500-16	Driveway Apron Detail Arterial/Collector Street

SECTION 500 - STREET AND PARKING FACILITIES CONSTRUCTION

501	GENERAL PROVISIONS

501.1	Applicability

This subsection contains minimum criteria to be met on all newly designed and constructed

public and private (open to general public) streets and parking lots in the City.

(a)	Traffic Impact Study

All subdivision, zoning and other site developments shall provide a street meeting

the minimum requirements of the Scottsbluff Municipal Code. Other arterial streets

shall be designed using the City of Scottsbluff traffic counts and the most recent

City of Scottsbluff Engineering Design Study.

(b)	Street design shall make adequate provision for culverts, drains and bridges,

underground utilities, sidewalks, trails and parkway landscaping and other

facilities and features located within or adjacent to the street sections.

501.2	Private Street Systems and Parking Lots

Private street systems and parking lots shall be subject to all requirements of these

Standards and Specifications, except that variances, as provided for in subsection

103.1(b), shall be allowed subject to the review and approval of the City Engineer.

501.3	Pavement Thickness Design and Technical Criteria

(a)	General

This subsection provides the basic criteria and design procedure for roadway

pavements. Recommended design methodologies for asphalt and Portland cement concrete

shall be based on the most recent City Engineer report on standard thickness for

asphalt and concrete street.

(b)	Preliminary Pavement Design Reports

For all land development approvals that involve a subdivision improvements agreement

for roadway construction, the applicant must provide a preliminary geotechnical

subgrade investigation report and a final pavement design report at the time of

final construction plan submittal that recommends typical pavement structural

sections based on the known site soil conditions and a valid Traffic Study.

(c)	Subgrade Investigation

1.	Field Investigation

The geotechnical investigation shall consist of borings or other suitable

method of sampling subgrade soils to a depth of at least three feet below

proposed subgrade elevation, at spacings of no more than 250 feet unless

otherwise accepted by the City Engineer. Samples shall be taken after grading

is completed and the subgrade is rough cut.

2.	Classification Testing

Each subgrade sample shall be tested to determine liquid limit, plastic limit,

plasticity index and the percentage passing the U.S. Standard No. 200 sieve.

Samples of sands and gravel may require gradation analysis for classification

determination. These data shall be determined using the following methods:

Liquid Limit - AASHTO T 89

Plastic Limit - AASHTO T 90

% Passing No. 200 - AASHTO T II

Gradation - AASHTO T 27

The results of these tests shall be used to calculate the AASHTO Classification

and Group Index using AASHTO M 145.

502	MINIMUM DESIGN CRITERIA

Street design, construction and right-of-way requirements shall conform to the provisions of

Municipal Ordinances 21-1-35 and 21-1-14 in conjunction with the most recent City Engineer

report on standard thickness for asphalt and concrete streets. All street design shall meet or

have approval of the Board of Public Roads Classifications and Standards Minimum Design

Standards.

502.1	Geometric Cross Section

Street cross sectional elements shall conform to the minimum design standards of the

Board of Public Roads Classifications and Standards and the City of Scottsbluff

Municipal Code. Collector and Arterial streets shall be constructed whenever the

alignment of the proposed street is generally the same as the collector and arterial

streets shown on the Classification Plan, and whenever a traffic engineering analysis of

the future traffic volumes indicates the need of a cross section greater than that of a

service street.

Additional ROW may be required to satisfy other criteria contained in these Standards and

Specifications. Areas outside the right-of-way shall be contour graded, compacted, and

sloped, as required for proper drainage, soil stability, and maintenance accessibility.

Cuts and fills proposed on slopes greater than four horizontal to one vertical shall

require supporting calculations done by qualified soils engineer based on a soils

analysis.

502.2	Half Streets

Where half streets have been approved by a variance issued by the City Engineer,

sufficient additional right-of-way shall be dedicated, and additional width shall be

constructed to allow sufficient paved width to accommodate two directions of traffic

and parking by offsetting the geometric cross section as shown on the detail drawings

for typical street cross sections.

502.3	Horizontal Alignment

Streets shall generally be aligned to bear a reasonable relationship to topography.

Horizontal curves shall conform to the street design criteria. Minimum spacing between

intersection centerlines shall be as described in the Municipal Code.

Streets shall intersect or connect to other streets as closely as possible to right

angles but shall not deviate more than 15 degrees from a right angle. Horizontal and

vertical alignment and ROW limits shall be coordinated so as not to obstruct sight

distance at intersections. Where two different street types connect, the larger curb

return radius shall apply.

502.4	Vertical Alignment

Gutter flowline grades shall be no less than 0.50 percent along curb returns, in cul-

de-sacs and bulb areas, and other areas where gutter flowline grades do not directly

parallel centerline profile grades.

502.5	Cul-De-Sacs

Lengths of cul-de-sacs are recommended to be no greater than 400 feet. Cul-de-sacs that

are proposed outside this range must be fully justified, based on the following

considerations and others that may arise in the course of review: 1.) intersection

vehicular traffic capacity; 2.) emergency vehicle response time; 3.) pedestrian trip time

to bus routes; 4.) travel distances for service and patrol vehicles; 5.) utility systems,

drainage, and open space access; 6.) solid waste collection vehicles; and 7.) fire

protection. Surface drainage shall be directed toward the intersecting street, or if this

is not reasonably practical, a drainage structure and a 20 foot easement shall be

provided at the end of the cul-de-sac.

502.6	Major Structures

Major structures, such as retaining walls and bridges, that are appurtenant to proposed

street construction, shall conform to the structural and loading requirements of the

AASHTO and the geometric and drainage requirements of the City Engineer. Plans and

supporting calculations for major structures must be prepared and sealed by a qualified

Nebraska registered engineer.

502.7	Design Element Coordination

Horizontal and vertical alignment continuity shall be provided between new and existing

streets to achieve safe and aesthetically pleasing transitions. Sufficient data on

existing facilities shall be depicted on plans, and limits of construction shall be

designated so as to assure that the desired continuity shall be achieved. Drainage and

utility facilities are to comply with all applicable sections of these Standards and

Specifications and are to be fully coordinated with the street design and proposed

construction; these facilities shall be staged to eliminate grade and alignment conflicts

and unnecessary damage to existing or newly constructed facilities.

502.8	Requirements of Other Jurisdictions

Where proposed street construction shall affect other agencies such as the NDOR, adjacent

cities and counties, or ditch companies, said construction shall be subject to the review

and approval of said agencies. Generally, where more than one requirement is imposed, the

more restrictive requirement shall govern. Exceptions must be authorized by the City

Engineer in writing.

503	EXCAVATION AND EMBANKMENT

503.1	General

The intent of this section is to specify materials, methods, and standards to be used in

the construction of embankments or excavations for City streets, or for other purposes,

as indicated on the drawings or contract documents. The work shall include: excavation,

embankment grading, compacting, clearing and grubbing, and the removal of topsoil,

trees, stumps, or other vegetation; removal and/or resetting of minor obstructions,

subgrade preparations; and any other work incidental for the construction of excavations

and embankments. All workmanship and materials shall be in accordance with the

requirements of these Standards and Specifications and in conformity with the lines,

grades, quantities, and the typical cross section shown on the plans, or as directed by

the City Engineer.

503.2	Clearing and Grubbing

Work shall consist of clearing, grubbing, removing and disposing of all vegetation and

debris within the limits of the project and such other areas as may be indicated on the

plans or required by the work, except such objects as are designated to remain or are to

be removed in accordance with other sections of these specifications. This work shall

also include preservation from injury or defacement of all vegetation and objects

designated to remain.

The City shall approve construction areas that are to remain. The Responsible Party

shall preserve all things designated to remain.

All surface objects and trees, stumps, roots and other protruding obstructions not

designated to remain shall be cleared and/or grubbed as required, to ensure complete

removal; however, nonperishable, non-toxic objects which shall be a minimum of two feet

below subgrade may remain when such objects shall not impede other subsurface operations.

Except in areas to be excavated, stump holes and other holes from which obstructions are

removed shall be backfilled with suitable material and compacted in accordance with these

Standards and Specifications. Materials and debris shall be disposed of in a manner

acceptable to the City Engineer. Burning of any materials shall not be permitted without

prior written approval of the City Engineer, the County Health Department, and Fire

Department.

The Responsible Party shall make all necessary arrangements for obtaining suitable

disposal locations. If disposal shall be at other than established dump sites, the City

Engineer may require the Responsible Party to furnish written permission from the

property Responsible Party on whose property the materials and debris shall be placed.

Branches on trees or shrubs shall be removed as directed by the City Engineer. Branches

of trees extending over the road bed shall be trimmed to give a clear height of 12 feet

above the road bed surface. All trimming shall be done by skilled workmen and in

accordance with good tree pruning practices.

The Responsible Party shall strip all areas where construction is to occur. Scalping

shall include the removal of material such as brush, roots, sod, grass, residue of

agricultural crops, sawdust, and other vegetative matter from the surface of the

ground.

Hedges shall be pulled or grubbed in such a manner as to assure complete and permanent

removal. Sod not required to be removed shall be thoroughly disked before construction of

embankment.

503.3	Removal of Miscellaneous Materials

(a)	General

The Responsible Party shall raze, remove, and dispose of all foundations, signs,

structures, fences, pavements, utilities, traffic signal materials and other

obstructions, which are designated for demolition within the project limits,

except for utilities and for materials which are to be preserved.

Pedestals and bases from sign posts and similar structures shall be removed to one

foot below the or proposed subgrade.

Where portions of structures are to be removed, the remaining shall be prepared to

fit new construction. The work shall be done in accordance with plan details and in

such a manner that materials to be left in place shall be protected from damage. All

damage to portions of structures which are to remain in place shall be repaired at

the expense of the Responsible Party. Reinforcing steel, projecting from the

remaining structure, shall be cleaned and aligned to provide bond with new

extension. Dowels are to be securely grouted with approved grout. All remaining

structures are to be delineated in the "As built drawings."

Removal of sign panel shall include all work necessary to remove the panel and its

attachment hardware from the existing installation.

Where culverts or sewers are to be left in place and plugged, the ends shall be

filled with concrete. Culvert and sewer ends are to be sufficiently filled to

prevent future settlement of embankments. All pipes shall be filled as directed

by the City Engineer.

Materials used in detour structures and supplied by the Responsible Party, shall

be the property of the Responsible Party. After the detour is abandoned, the

Responsible Party shall completely remove the detour structure and shall dispose of

materials according to these Standards and Specifications.

(b)	Bridges, Culverts and Other Drainage Structures

Bridges, culverts, and other drainage structures in use by traffic shall not be

removed until satisfactory arrangements have been made to accommodate traffic and

storm drainage.

Unless otherwise directed, the substructures of existing structures shall be removed

down to one foot below natural stream bottom or ground surface. Where such portions

of existing structures lie wholly or in part within the limits of a new structure,

they shall be removed as necessary to accommodate the construction of the proposed

structure. Steel, precast concrete, and wood bridges shall be carefully dismantled

without unnecessary damage.

(c)	Pipe

Unless otherwise provided, all pipe shall be carefully removed and cleaned; every

precaution shall be taken to avoid breaking or damaging the pipe. Pipes to be relaid

shall be removed and stored, when necessary, so that there shall be no loss or

damage before relaying.

When removing manholes, catch basins and inlets, any live sewer connected with these

items shall be properly reconnected, and satisfactory bypass service shall be

maintained during such operation.

(d)	Pavements, Sidewalks, Curbs, Etc.

Portland Cement Concrete (PCC) or asphaltic concrete that is to remain shall be cut

in a straight, true line with a vertical face. PCC or asphaltic concrete may be cut

with a cutting wheel, jackhammer (demolition of structure following surrounding

clean cuts), or saw, or may be broken to the directed point of removal. The

Responsible Party shall be responsible for the cost of removal and replacement of

all overbreak as identified on the construction plans.

If the Responsible Party cannot maintain a straight, true break line by other means,

the City Engineer shall order sawing. The sawing shall be done carefully, and all

damages to PCC or asphaltic concrete to remain in place, which are caused by the

Responsible Party's operations, shall be repaired by the Responsible Party at his

expense. The minimum depth of saw cuts in concrete shall be two inches.

(e)	Backfill

Except in areas to be excavated, all cavities left by structure removal shall be

backfilled with suitable material and compacted in accordance with these Standards

and Specifications. Jetting or puddling shall not be allowed, except in landscaped

areas as specified in Section 800.

503.4	Protection of Utility Lines and Structures

The Responsible Party shall take proper precautions at all times to protect utility

lines, manholes, valve boxes, survey monuments, and other structures which are present

or can be determined to be present by examination of the appropriate maps of the utility

companies. The Responsible Party shall notify the appropriate company whenever working

near gas mains or buried electrical cable. The telephone company or cable television

company shall be notified by the Responsible Party when the presence of buried cable is

suspected in the construction area.

The Responsible Party shall be held responsible for the repair or replacement of

structures damaged. Hand excavation shall be used where necessary. All existing manholes

and valve boxes shall be adjusted to final grade by the Responsible Party. Where riser

rings are installed, they shall have a wide, slotted flange for support and be equal to

Clay Bailey #3100, or as approved by the City Engineer. If any existing manhole rings

and covers or valve boxes are found to be defective, they shall be reported to the City

and replaced at the direction of the City Engineer.

503.5	Protection of Public and Private Installations

The Responsible Party shall take proper precautions at all times for the protection of

and replacement or restoration of driveway culverts, street intersection culverts or

aprons, storm drains or inlets, fences, irrigation ditches, crossings and diversion

boxes, mail boxes, shrubbery, flowers, ornamental trees, driveway approaches, and all

other public and private installations that may be encountered during construction.

The Responsible Party shall have the responsibility of providing each property with

access to and from the property during the time of construction. Existing driveways

shall be cut, filled, and graded as required and as directed by the City Engineer to

provide permanent access. Existing driveways shall be resurfaced with the presently

existing type of surfacing whenever the existing surface is destroyed.

503.6	Excavation and Embankment

Excavation of whatever substances are encountered within the limits of the project shall

be performed to the lines and grades indicated on approved plans. All excavated areas

shall be graded in a manner that shall permit adequate drainage. Whenever practicable,

all suitable material removed from the excavations shall be used in the formation of

embankments, for backfilling, and for other purposes. Where material encountered within

the limits of the work is considered unsuitable, such material shall be excavated below

the grade shown on the drawings, or as directed by the City Engineer, and replaced with

suitable material. All unsuitable excavated materials, and any surplus or excavated

material which is not required for embankments, shall be disposed of by the Responsible

Party.

The construction of embankments by deposition, placing, and compacting materials of

acceptable quality above the natural ground or other surface shall be in accordance

with the lines, grades, and cross sections shown on the approved plans and/or as

required by the City Engineer. Each lift of the embankment material shall not exceed

eight inches in loose depth. The Responsible Party shall thoroughly mix the different

materials to secure a uniform moisture content and to insure uniform density and proper

compaction. Each layer shall be thoroughly compacted by roller or vibratory equipment

which is suitable for the type of embankment material, to the densities specified in

these Standards and Specifications.

503.7	Borrow

In the event sufficient suitable fill material is not obtainable within the limits of the

project to provide all the embankment required, the Responsible Party shall furnish such

additional fill material (borrow) to complete the designated embankment. Borrow shall be

an acceptable type of embankment material, an (SM), or coarser, as determined by the

Unified Soil Classification System, and shall be approved by the City Engineer before

being placed.

503.8	Subgrade

The bottom of the excavation for the pavement, or top of the fill, shall be known as the

pavement subgrade and shall conform to the lines, grades, and cross sections shown on

the approved plans.

Prior to the street being excavated, all service cuts shall be tested to see if the

backfill meets density requirements. If deficient, they shall be recompacted and brought

up to the density specified.

After excavation and embankment is completed and the subgrade brought to final grade,

it shall be rolled with a rubber-tired or sheep foot roller as required to bring the

subgrade to the required density and stability. All soils shall be compacted to a minimum

of 95 percent of maximum dry density as determined by AASHTO T-99. Additional wetting may

be required when the minimum water requirement is not sufficient to produce a stable

condition in the subgrade soil.

No paving, subbase, or base shall be placed on soft, spongy, frozen, or unstable subgrade

which is considered unsuitable by the City Engineer.

Heavy construction equipment or loaded trucks shall be driven over the finished subgrade

and deflections noted. Soft and yielding material and portions of the subgrade which show

deflection shall be scarified and re-rolled or shall be removed and replaced with

approved course subgrade material, then placed and compacted as specified herein.

Subgrade shall not be approved for base course construction until it is uniformly stable

and unyielding.

503.9	Subbase Construction

(a)	Materials

Subbase material shall be composed of granular material consisting, essentially, of

sand, gravel, rock or a combination of such materials. The coarse portions of the

material shall be sound fragments of the crushed or uncrushed materials enumerated

above. Supplied material shall be a well-graded mixture containing sufficient soil

mortar, crushed dust, or other proper quality binding material which, when placed

and compacted in the roadway structure, shall result in a firm, stable foundation.

Material composed of uniform size particles, or which contains pockets of

excessively fine or excessively coarse material, shall not be acceptable for use.

This material need not be crushed but shall be graded within the following limits:

Standard-Size of Sieve         % By Weight Passing Sieve

1 inch	                100

3/4 inch	                90 - 100

No. 10 	                40 - 60

No. 40                	                20 - 40

No. 200	                5 - 13

Liquid Limit 	                35 Maximum

Plasticity Index	                6 Maximum

(b)	General

The specifications presented in this subsection are performance oriented. The

objective in setting forth these specifications is to achieve an acceptable quality

of roadway structures. All sources, mined or manufactured, must be annually approved

by the City Engineer as having met the appropriate material performance

specifications. This approval is a condition of using those material sources for

public and private improvement construction.

(c)	Violations of Approval Conditions

The City Engineer may order random tests of materials used in the City to verify

compliance with material specifications. Any and all material used to construct

public and private improvements that is not from a certified source, or that is

from a certified source and fails one or more random material tests, shall be

subject to complete removal. The extent of the material to be removed shall be

at the discretion of the City Engineer.

(d)	Use of Materials Not Listed

Materials listed in this subsection and provided with a set of specifications are

those deemed to be the primary structural materials commonly or typically used in

public and private improvements. Ancillary public and private improvement materials

such as manufactured paints and coatings, bonding agents, sealers, gaskets,

insulating materials, etc. should be in compliance with NDOR material specifications

for the appropriate materials employed. Alternative materials for construction may

be proposed for use, except where expressly prohibited. Decisions on acceptability

of alternative materials shall be made by the City Engineer.

(e)	Construction

The construction of subbase shall consist of furnishing and placing approved subbase

material to form a stable foundation on which to construct pavement, in conformity

with the lines, grades and typical cross sections shown on the plans, and as staked

by a surveyor under the direct supervision of a Nebraska registered surveyor or

engineer. In addition, subbase material shall be used to replace unsuitable

foundation materials at locations shown on the plans, or as directed by the City

Engineer.

Each layer of material shall be placed and spread so that after compaction it shall

conform to the width and crown of the typical cross sections. The wetting of subbase

layers shall be done with sprinkling equipment of a type which insures uniform and

controlled distribution of the water. All wetting shall be done by uniformly

sprinkling each layer of material being placed with only that amount of water needed

to obtain maximum density of the material.

Travel may be allowed over subbase to assist in compaction of the material. Mixing

and blading of the subbase material on the street shall be required if the material

is spotty and non-uniform. However, blading shall be held to a minimum in order to

avoid the floating of the heavier aggregate particles to the surface.

Concurrently with the wetting operations, the material shall be uniformly compacted

by rolling. Rolling equipment shall consist of one or more of the following: rubber

tired roller, sheep foot roller and flat wheel steel roller.

504	BITUMINOUS CONSTRUCTION

504.1	General

The intent of this section is to specify materials and methods to be used for the

construction, overlaying, sealcoating and pavement rejuvenating of streets, parking

lots, walks, and other miscellaneous work requiring the use of aggregates. The work

covered shall include general requirements that are applicable to aggregate base

course, bituminous base and pavements of the plant mix type, bituminous prime coat,

rejuvenating applications, and asphalt concrete overlay. All workmanship and material

shall be in accordance with requirements of these Standards and Specifications and in

conformity with the lines, grades, depths, quantity requirements, and the typical

cross section shown on the plans or as directed by the City Engineer.

504.2	Subbase Course

This item shall consist of a foundation course composed of crushed gravel or crushed

stone and filler, constructed on the prepared subgrade when specified. Materials and

construction shall be in accordance with the requirements of these specifications.

The subbase material shall be placed on the previously prepared subgrade at the

locations and in the proper quantities to conform to the typical cross sections as

shown on the plans and as directed by the City Engineer. Placing and spreading shall

be done by means of a spreader machine, moving vehicle, motor grader, or by other

approved equipment methods. The material shall be placed without segregation. Any

segregated areas shall be removed and replaced with uniformly graded material at the

Responsible Party's expense.

The base material may be placed in lifts of up to six inches, providing that after

compaction, uniform density is obtained throughout the entire depth of the lift. If

the required depth exceeds six inches, it shall be placed in two or more lifts of

approximate equal thickness. If uniform density cannot be obtained by six inch lifts,

the maximum lift shall not exceed four inches in final thickness.

Base material shall not be placed on a foundation that is soft or spongy or one that

is covered by ice or snow. Base material shall not be placed on a dry or dusty

foundation where the existing condition would cause rapid dissipation of moisture from

the base material and hinder or preclude its proper compaction. Such dry foundations

shall have water applied to them and shall be reworked or recompacted.

Rolling shall be continuous until the base material has been compacted thoroughly, to

obtain minimum dry density of 100 percent as determined by AASHTO T-99. Water shall be

uniformly applied as needed during compaction to obtain optimum moisture content and to

aid in consolidation. The surface of each layer shall be maintained during the compaction

operations in such a manner that a uniform text is produced and the aggregate are

firmly placed.

The finished subbase surface shall be smooth and free of ruts and irregularities, and

shall be true to grade and crown as shown on the plans or as directed by the City

Engineer. The subbase shall be maintained in this condition by watering, drying, rolling,

or blading or as the City Engineer may direct until the surfacing is placed.

504.3	Hot Bituminous Pavement

All pavement shall be hot bituminous pavement of the plant mix type unless otherwise

approved in writing by the City Engineer. materials and construction shall be in

accordance with the NDOR "Standard Specifications for Highway Construction", Section 507,

and the following requirements:

1.	The asphalt cement shall be AC 10 or 20 penetration grade.

2.	The gradation of the mineral aggregate shall be in accordance with Asphaltic

Concrete Mix Type 14.

3.	The mix shall conform to the job mix formula specified by the City Engineer for

the specified materials, if a current job mix formula is available. A copy of the

mix formula shall be submitted to the City Engineer for review and approval at least

seven days prior to starting paving work.

All testing done throughout this construction period which is necessary to assure

conformance of materials and workmanship to the specifications shall be at the

Responsible Party's expense. Two copies of all test reports shall be submitted directly

to the City Engineer.

In the event that a current job mix formula is not available for the materials proposed

for use, the Responsible Party shall submit a job mix formula prepared by a recognized

testing laboratory for approval of the City Engineer. A report giving the properties of

the materials and certifying their conformance to or deviations from the requirements of

the specifications shall accompany the job mix formula.

When tested in accordance with the requirements of ASTM D-1559, the mixture shall conform

to the following limits:

Stability (minimum)	              1000

Flow (minimum) hundredths of an inch         8

Flow (maximum) hundredths of an inch         16

Percent voids	              3 to 6

Percent voids filled with bitumen            75 to 85

Determination of the effect of water on the cohesion of the bituminous mixture shall be

made in accordance with AASHTO T-165. Retained strength shall be a minimum of 75. The use

of an "anti-stripping" admixture to improve the retained strength characteristics shall

be permitted only by written permission of the City Engineer.

All commercial testing and laboratory work necessary to establish the job mix formula and

all testing necessary to assure conformance of materials and workmanship to the

requirements of the specifications throughout the construction period shall be performed

at the Responsible Party's expense. Two copies of all test reports shall be submitted

directly to the City Engineer.

(a)	Hot Bituminous Pavement

This material shall consist of a mixture of aggregate, filler (if required) and

asphalt cement. The aggregate mixture shall meet the grading requirements of NDOR

specifications and the job mix formula. Tests on the aggregates for cleanliness,

abrasion loss and fractured faces shall meet the requirements shown below. The job

mix formula shall establish a single percent passing each sieve size, an optimum

percent of asphalt cement to be added to the aggregate and a recommended mix

temperature when discharged at the plant.

TABLE 500-1

MATERIAL SPECIFICATIONS FOR HOT BITUMINOUS PAVEMENT

Sieve Size or                      Percent Passing or         Test Requirement

Test Procedure                     E or C Mix                 E or CX Mix

3/4"                               100                        ---

1/2"                               70-95                      100

#4                                 44-72                      50-78

#8                                 30-58                      32-60

#200                               3-9                        3-9

% Wear, AASHTO T-96                45, Max.                   45, Max.

One Crushed Face on +4             50, Min.                   50, Min.

Index of Retained                  75, Min.                   75, Min.

Strength ASTM D-1075

1.	Aggregates shall not contain clay balls, organic matter, or other deleterious

substances.

2.	After the job mix formula is established, all mix furnished for the project shall

conform to it within the following range of tolerances.

TABLE 500-2

MIX TOLERANCES

Maximum Size                       +/-0 percentage points

Passing No. 8 and larger           +/-8 percentage points

No. 8 to No. 100                   +/-6 percentage points

Passing No. 200                    +/-3 percentage points

Asphalt Content                    +/-0.5 percentage points

Discharged Mix Temperature         +/-20 F

3.	An additive may be used to meet the requirement for Index of Retained Strength, if

necessary. Such additives may be hydrated lime, Type I Portland cement, or anti-

stripping agents approved by the NDOR.

4.	The asphalt cement used shall be grade AC-10 or 20.

A mix design, including the job mix formula, shall be submitted for review and

approval a minimum of seven (7) days prior to placing mix on the project. The mix

design shall be performed using either the Marshall or Hveem procedures as outlined

in the Asphalt Institute, "Mix Design Methods for Asphalt Concrete" (MS-2). Mix

design parameters for each of the procedures as shown in Table 500-12.

TABLE 500-3

MIX DESIGN CRITERIA FOR ASPHALT CONCRETE

Marshall (50 blows)     Hveem

Test                                AASHTO T 245            AASHTO T 246

Strength            	     1,500, Min.             Rt 90, Min.

Flow, 0.01"         	     8-18                    ---

VMA	 	     14, Min.                14, Min.

Air Voids, Total Mix %     	     3-6                     3-6

504.4	Tack Coat

When tack coat is specified on the approved plans or required by the City Engineer, all

materials and construction shall be in accordance with the requirements of the NDOR

Standard Specifications, Section 502. Bituminous material shall be SS-1H emulsion,

diluted by mixing one gallon of SS-1H emulsion with one gallon of clean water, applied

at the rate of 0.05 to 0.15 gallons per square yard.

504.5	Seal Coat

When seal coat is required, all materials and construction shall be in accordance with

the requirements of the NDOR Standard Specifications, Section 505. The type of bituminous

material, cover aggregate, and rates of application shall be as shown on the approved

construction plans.

504.6	Rejuvenating Agent

When a rejuvenating agent is specified on the approved construction plans or required by

the City Engineer, all materials and construction shall be in accordance with the

requirements of the special provisions for the project. The rejuvenating agent shall be

as shown on the approved construction plans or as specified by the City Engineer.

504.7	Heating and Scarifying

When heating and scarifying treatment is specified on the approved construction plans

or required by the City Engineer, all materials and construction shall meet the

requirements of the special provisions.

504.8	Grinding

Grinding shall consist of "milling", "grinding", or "cold planing" the existing pavement

surface to establish a new surface profile and cross section in preparation for an

overlay. All construction shall be in accordance with the requirements of the NDOR

Standard Specifications, Section 510. The dimensions of the milling shall be indicated on

the approved plans.

Grinding around utility castings to the depth of cut before and after encountering the

castings shall be included in the area of the pavement surface ground. The Responsible

Party may choose to remove the entire existing bituminous pavement around the castings

where grinding is not completed, and replace it with bituminous surface course placed

and compacted in two inch lifts. The Responsible Party shall vertically cut the limits

of the area to be patched, mechanically compact the existing base course, and prime the

bottom and vertical edges before backfilling.

The grinding machine shall be a power operated, self-propelled machine, having a cutting

drum with lacing patterns that shall attain a grooved surface and produce grinding chips

of less than one inch in size. The grinding machine shall be equipped with a pressurized

watering system for dust control. The equipment shall be a type that has successfully

performed similar work.

The Responsible Party shall remove the cuttings immediately behind the grind machine by

belt loader, end loader, power sweeper and/or by hand. The removed material shall be

disposed of as approved by the City Engineer.

The cleaning equipment shall be a type which shall efficiently remove all loosened

material, load it into trucks for hauling and spreading, and utilize a watering system

for dust control. Because of the nature of the streets to be ground and the traffic

restrictions, a beltloader followed by a power sweeper and manual sweeper is the most

desirable method. Flushing into the City's storm sewer system as a means of cleanup shall

not be allowed.

It shall be the responsibility of the contractor to furnish flagger(s) to direct traffic

when his equipment is operating over or adjacent to the roadbed being used by the

traveling public.

The flagger(s) shall be properly attired with a traffic-control colored vest and equipped

in accordance with the requirements of the plans and specifications, and shall position

themselves at all times standing on or immediately adjacent to the traveled roadway while

work operations are in progress. The flagger(s) should be familiar with the contents of

the Nebraska Department of Roads publication, "Instructions to Flagmen".

When a detour is not provided in the plans, the milling operation shall be performed in

a manner that will not create undue traffic hazards with one lane open to traffic at

all times.

When the milled surface is open to traffic and the milling has resulted in the

obliteration of the centerline stripe, the contractor will be required to place and

maintain a temporary reflectorized traffic centerline. This work shall consist of

installing and removing reflectorized temporary pavement lines of the color, width and

line configuration shown in the plans or as designated by the engineer.

The temporary pavement marking tape shall be made with a tape-like material manufactured

from a thin sheet of malleable aluminum, coated with a white or yellow binder,

reflectorized with high index of refraction glass beads and backed with a pressure-

sensitive adhesive.

Unless otherwise specified, the temporary pavement marking tape shall be four inches wide

and the reflectorizing glass beads shall have an index of refraction of not less than

1.90. The pressure-sensitive adhesive shall register not less than one pound when the

adhesive strength is tested using method A as outlined in ASTM D1000. It shall be capable

of being easily applied by hand.

The temporary pavement marking may also be made from a mixture of high quality polymeric

materials and pigments, with glass beads throughout the pigmented portion of the film,

and a reflective layer of high index of refraction glass beads bonded to the top surface.

The film shall be precoated with a pressure-sensitive adhesive. A non-metallic medium

shall be incorporated to facilitate removal. Unless otherwise specified, the temporary

pavement marking shall be 4 inches wide and the reflectorizing glass beads shall have an

index of not less than 1.90.

The materials used shall be capable of being easily applied and removed. The contractor

shall be required to demonstrate that the properly applied pavement marking adheres to

the roadway under climatic and traffic conditions normally encountered in the

construction work zone.

505	CONCRETE PAVEMENT

The installation of concrete pavement, including materials, equipment, foundation and

construction methods shall be in conformance with Section 601, "Concrete Pavement" of the NDOR

Standard Specifications, except as modified herein or as modified by the

approval of the City Engineer.

Section 600 of these Standards and Specifications must be followed for concrete work. Concrete

pavements shall be installed as shown on the approved plans or as approved by the City

Engineer. When concrete pavement is constructed on a curve, flexible forms shall be used unless

otherwise directed by the City Engineer. The Responsible Party shall furnish steel pins to use

in setting grades for concrete pavement.

505.1	Portland Cement Concrete Pavement

This material shall consist of a mixture of coarse and fine aggregates, Portland cement,

water and other materials or admixtures as required. NDOR Class "47-B" mix shall be used.

1.	Portland cement shall comply with the NDOR requirements. The type of cement shall

be Type I or Type II Low Alkali. Table 2.2.3 in Chapter 2.2 of ACI 201 indicates

recommendations for sulfate resistance.

2.	Fine aggregates shall meet NDOR Standard Specifications.

3.	Coarse aggregates shall meet NDOR Standard Specifications.

4.	Fly Ash shall comply with NDOR Standard Specifications, if use is approved by City

Engineer.

5.	Water shall meet the requirements of NDOR Standard Specifications.

6.	Air entraining and chemical admixtures shall meet the requirements of NDOR Standard

Specifications. No chloride containing additives shall be permitted.

7.	Curing materials shall be white pigmented liquified membrane curing compound and

meet the requirements of AASHTO M 148.

8.	Reinforcing steel shall meet the requirements of NDOR Standard Specifications,

grade 40 minimum.

9.	Minimum compressive strength shall be 4000 psi; minimum modulus of rupture or

flexural strength shall be 600 psi.

505.2	Aggregate Base Course Material

If aggregate base course is required it shall be specified in the project special

provisions.

505.3	Subgrade Investigation and Pavement Design Report

If the current City Engineer's report on Standard Thickness for Asphalt and Concrete

Streets does not include the area to be paved, the City Engineer may require a Subgrade

Investigation and Pavement Design Report.

506	APPURTENANT CONCRETE STRUCTURES

506.1	General

Curb, curb ramps, gutter, sidewalk, cross pan, and driveway construction shall conform to

all applicable provisions of these Standards and Specifications and detail drawings.

506.2	Materials

(a)	Concrete Cement

All concrete cement materials, reinforcing steel, and concrete work shall conform

to the requirements of Section 600 of these Standards and Specifications.

(b)	Forms

Forms may be wood or metal and shall have a depth equal to or greater than the

slab thickness. The face of curbs shall be formed, unless otherwise permitted by

the City Engineer. Forms shall have a cross section and strength and be secured

so as to resist the pressure of the poured concrete without springing or settlement.

The connection between sections shall be performed by a method in which the joint

thus formed shall be free from movement in any direction. Each section of form shall

be straight and free from warps or bends. The maximum deviation of the top surface

shall not exceed 1/8 inch and the inside face not more than 1/4 inch from a straight

line in ten feet. Approved flexible forms may be used for construction.

506.3	General Requirements

(a)	Curb and Gutter Section

The section to be constructed shall be as identified on the approved plans or as

shown on the detail drawings.

(b)	Sidewalks and Bikeways

Sidewalks shall be four inches thick if detached, or six inches thick if attached

and constructed to the dimensions shown on the approved construction plans. All

areas of sidewalk that shall be crossed by driveways shall be constructed with six

inch thick concrete. Bikeways shall be a minimum of five inches thick.

(c)	Crosspans and Curb Return Fillets

Crosspans and curb return fillets shall be six inches thick in residential areas

and eight inches thick in commercial and industrial areas. Typical cross pan

sections are shown on the detail drawing. Where unusual conditions prevail,

additional reinforcing steel and special joints may be required by the City

Engineer.

(d)	Curb Cuts and Driveways

In commercial and industrial areas, curb cuts shall be provided at all driveway

locations and at additional locations, as shown on the approved plans. Construction

of curb cuts and spacing shall be as shown on the detail drawings.

(e)	Curb Ramps

Curb ramps shall be included on all new construction and reconstruction of curbs.

Curb ramps shall be constructed as shown on the detail drawing.

506.4	Construction Requirements

(a)	Staking and Grade Control

Control stakes shall be set by field parties under the supervision of a Nebraska

registered professional engineer or land surveyor provided by the Responsible

Party or by the City Engineer. These field parties shall be available to check field

control and to provide assistance to the Responsible Party. A set of approved plans

shall be kept on the job site at all times by the Responsible Party. All survey data

shall be provided to the City upon request.

It shall be the responsibility of the Responsible Party to maintain the grade and

alignment as shown on the approved plans. The alignment and grade elevation of

forms shall be checked, and any necessary corrections shall be made before placing

the concrete. When any form has been disturbed or any subgrade thereunder has become

unstable, the form shall be reset and rechecked.

(b)	Excavation and Embankment

Excavation or fill shall be made to the required grade, and the base on which the

curbing section is to be set shall be compacted to a smooth, even surface. All

material placed in fill and the top six inches of the subgrade in cut sections

shall be compacted to at least 95 percent of maximum dry density as determined by

ASTM D-698 or AASHTO T-99. Where spongy, frozen or unsuitable materials are

encountered which shall not provide a stable subgrade, the material shall be removed

and replaced with suitable material and compacted to the specified density.

The subgrade shall be compacted within the forms by a vibratory compactor or

other approved method whenever any loose subgrade material is present. Immediately

prior to placing the concrete, the subgrade shall be tested for conformity to the

specified cross section. Materials shall be removed or added to bring all portions

of the subgrade to the correct elevation. The subgrade shall be thoroughly compacted

and again tested for proper cross section. Concrete shall not be placed on any

portions of the subgrade that has not been inspected by the City Engineer, or

designee, for correct elevation and proper compaction. The subgrade shall also be

cleared of any loose material that may have fallen on it.

The subgrade shall have proper moisture content to a depth of six inches at the time

the concrete is placed. It shall be thoroughly wetted a sufficient amount of time in

advance of the placing of the concrete to insure there shall be no puddles or

pockets of mud when the concrete is placed.

(c)	Form Setting

Forms that have become worn, bent, or broken shall not be used. The Responsible

Party shall have set and graded a minimum length of 300 feet of forms prior to

placing concrete. In cases where the length of one run is less than 300 feet, the

Responsible Party shall set and grade forms for the entire run.

On curves with radii of 200 feet or less, flexible forms which can be readily

formed to the desired radius shall be used. Face forms shall be performed to the

proper radius. In any case, care shall be exercised to insure the maintenance of

the required cross section around the entire radius.

The Responsible Party shall provide an approved metal straight edge, 10 feet in

length, to check the alignment of the forms prior to placing the concrete and also

to check the concrete surface during the finishing operation.

Forms shall remain in place at least 12 hours after concrete has been placed against

them, or for a longer period if so directed by the City Engineer. Crowbars or other

heavy tools shall not be used against green concrete in removing the forms. Forms

shall be thoroughly cleaned before reoiling and reuse. Forms shall be thoroughly

coated with an approved form release agent prior to placement of concrete.

(d)	Concrete Placement

When placed in the forms the concrete shall be properly graded with the forms and

shall at no time deviate more than one-quarter inch from a straight edge 10 feet in

length. The concrete shall be placed on damp but not wet or muddy subgrade. The

operation of depositing the concrete and compacting it shall be conducted so that

the concrete shall be smooth and dense, free from honeycomb and free from pockets

of segregated aggregate. Sections of segregation or honeycomb revealed by removal of

the forms shall be removed and replaced or otherwise repaired to the satisfaction of

the City Engineer. At the end of the day, or in case of an unavoidable interruption

of more than 30 minutes, a transverse construction joint shall be placed at the

point of stopping work, provided that the section on which work has been suspended

shall not be less than five feet. Sections less than five feet in length shall be

removed. Concrete shall not be placed when the weather is stormy, dusty, or

otherwise inclement to the point that it precludes good workmanship.

(e)	Joints

All joints shall be constructed straight and plumb and shall extend through the

entire section from edge to back and and to depths specified herein.

1.	Expansion Joints: Expansion joint filler, which is one-half inch thick,

performed, nonextruding bituminous-treated fiber board conforming to AASHTO

Specification M-213, shall be used to form transverse expansion joints.

Expansion joints shall be constructed at each tangent point of the curb radius,

at each end of valley gutters, at approximately 150 foot intervals on tangent,

or at other points as may be directed by the City Engineer. Expansion joints

shall be formed at the contact of the new construction with concrete driveways,

intersecting sidewalks, or other unyielding structures unless otherwise

directed.

2.	Block Joints: The curb and gutter or curbwalk shall be divided into blocks not

less than five feet nor more than 8 feet long using metal templates not less

than one-sixteenth inch nor more than one-quarter inch thick. Templates shall

be a minimum of four inches deep. The block length to be used shall be approved

by the City Engineer prior to starting construction and shall be maintained

constant throughout the project. The templates shall be designed to attach

securely to the forms in such a manner as to prevent movement while the

concrete is being placed and consolidated. Templates shall be removed prior

to the concrete taking its initial set.

If curbing machine or other methods not requiring the use of templates are

approved, dummy joints formed by a jointing tool or other acceptable means

shall be used. Dummy joints shall extend into the concrete for at least 1/3

of the depth and shall be approximately one-eighth inch wide.

3.	Construction Joints: As required at the end of a day's run, construction joints

shall be made at right angles to the longitudinal axis of the curb and gutter

and shall be located at the regular spacing designated for block joints unless

otherwise specifically permitted by the City Engineer. In no case shall any

length of curb and gutter be less than five feet between joints. Construction

joints shall be formed by use of a bulkhead or divider which shall be removed

before continuing with the next run. The construction joints shall be edged to

form a recess for sealing compound similar to that for expansion joints.

(f)	Finishing

Where applicable, finishing shall be done with a metal screed designed to give

proper shape to the section as detailed. Particular care shall be used to finish

the gutter flowline to a true, uniform grade. When using face forms, they shall be

left in place until the concrete has hardened sufficiently so that they can be

removed without injury to the curb.

The Responsible Party shall use at all times, a 10 foot straightedge for finishing

curb and gutter sections. When irregularities are discovered, they shall be

corrected by adding or removing concrete. All disturbed places shall be floated with

a wooden or metal float which is not less than three feet long and not less than six

inches wide, and again straightened. No water or cement shall be added to the

surface of the concrete to aid in finishing. Before final finishing is complete and

the concrete has taken its initial set, edges of the concrete and joints shall be

carefully finished with an edger having an 1/8 inch radius. Concrete shall be

finally finished with a wood float and lightly broomed to a slightly roughened

surface. On grades less than one percent, the Responsible Party shall check for

depressions before final finish so that no water holes exist. Any water holes or

"bird baths" larger than one square foot and deeper than 3/8 inch shall be cause

for removal and replacement of the defective sections of concrete.

(g)	Curing

Curing shall be accomplished in accordance with these Standards and Specifications

for concrete work (Section 600).

(h)	Protection Against Vandalism

It shall be the responsibility of the Responsible Party to protect all concrete

work against damage or vandalism. When required, a guard shall be stationed over

fresh work until the concrete is sufficiently set to prevent its being marked by

plastic deformation of the exposed surface of the concrete. Expense of the guard

shall be borne by the Responsible Party. Concrete damaged in any way by vandals

shall be removed and replaced at the Responsible Party's expense.

(i)	Cleanup

Within 48 hours after forms are removed, the area behind the sidewalk or curb shall

be cleaned, backfilled and graded to provide a smooth even surface, equal to or

better than the pre-construction condition.

(j)	Concrete Testing

Routine testing shall be accomplished in accordance with these Standards and

Specifications, Section 600. In the case of questionable concrete materials or work,

the City Engineer may direct that core tests be made on all questionable concrete

placement. The expense of the tests shall be borne by the Responsible Party. If the

concrete tested shows inadequate strength or other deficiencies, it shall be

removed and replaced by the Responsible Party at his expense. If any core shows a

deficiency of thickness greater than one-half inch, exploratory cores shall be

taken in five foot increments, and all concrete deficient more than one-half inch

shall be removed and replaced by the Responsible Party.

507	INSPECTION

507.1	General

All work shall be inspected by the City. Whenever any work is not performed in accordance

with City requirements, the City Engineer shall give the Responsible Party written notice

listing deficiencies to be corrected. If the deficiencies are not corrected within the

time limit specified in the notice, the City Engineer may evoke enforcement options

authorized by City ordinance and resolution, or bonds under which the work be being

performed.

507.2	Required Inspections

Adequate inspections assure compliance to City requirements and are the basis for the

City's recommendation that said streets be given initial acceptance and for release of

bonds. It is the responsibility of the Responsible Party to contact the City Engineer

48 hours in advance of the required inspections. Required inspections include:

1.	Culverts - trenching, grade, bedding, installation, backfill and compaction.

Inspection to be requested when backfill is completed to one-half the depth of

the culvert.

2.	Concrete - finished excavation, grade, forming, reinforcing steel.

3.	Structures - concrete pour, surface finish, and test cylinders. Three inspections

are required: (1) prior to placing steel; (2) prior to concrete pour; and (3) after

final pour.

4.	Street - five inspections are required: (1) subgrade; (2) subbase; (3) base course;

(4) prime, and (5) paving, all of which are required prior to proceeding with the

next phase. Locations of required samples for testing shall be designated by the

City Engineer.

507.3	Required Testing

When required by the City Engineer, a recognized and approved testing firm shall certify

the quality of materials or construction. All testing shall be by recognized methods as

specified in these Standards and Specifications, and shall be at the Responsible Party's

expense or as directed by the City Engineer.

507.4	Utility Installations

Prior to the installation of street subbase, base, paving and concrete materials, utility

installations shall be made, service lines stubbed to the right-of-way line, placement of

conduit, and all trenches shall be backfilled and properly compacted.

507.5	Street Lighting

At the time of inspection, all street lights shall be in place as shown on the approved

plans and shall be operating as set forth in subsection 707.5 of these Standards and

Specifications.

508	ROADWAY INSPECTION AND TESTING

508.1	General

NDOR Standard Specifications, most recent edition, special provisions and revisions

thereto and as amended by the City Engineer shall apply.

All test and inspection results performed by the testing firm in the employment of the

Responsible Party shall be submitted to the City Engineer or his field representative

at the time of testing or within fifteen working days after the testing or retesting

date.

508.2	Inside Rights-of-Way

Any work performed inside right-of-way and associated easements shall be tested by a

materials testing firm which employs a full time Professional Engineer, registered in

the State of Nebraska, who directly supervises work of the firm. Concrete technicians

must be ACI or equivalent Level I technicians. The costs of testing and associated

reporting are paid by the Responsible Party or as directed by the City Engineer.

508.3	Test Listing

The testing of all materials and construction shall be in conformance with the

appropriate AASHTO and ASTM specifications. A partial list of approved testing methods

includes:

TEST                                AASHTO         	ASTM

Atterberg 	T 89 & T 90	D 4318

Gradation Analysis	T 27	D 422

(except hydrometer)

CBR			T 193	---

R-value (subgrade & base)	T 190	D 2844

Marshall Stability	T 245	D 1559

Rt value		T 246	D 1560

Compaction Curve (standard)	T 99	D 698

Compaction Curve (modified)	T 180	D 1557

Compaction Curve (CTAB)	T 134	---

Field Density Test (Sand Cone)	T 191	D 1556

Field Density Test (Nuclear)	T 238/T 239	D 2922/D 3017

Field Density Test (Balloon)	T 205	D 2167

Concrete Slump	T 119	D 143

Concrete Air Content	T 152	D 231

Concrete Field Specimens	T 23	D 31

Concrete Compressive Strength	T 22	D 39

Concrete Sampling	T 141	D 172

Strength of Soil-Lime Mixtures	T 220	---

Asphalt Flow	T 245	D 1559

Voids		T 245	D 1559

508.4	Roadway Subgrade Preparation

(a)	Compaction

The subgrade shall be free of organic material and shall be scarified to a minimum

depth of six inches, or as stated in the Pavement Design Report, moisture treated

to within two percent of optimum moisture content and compacted. Table 500-10 shall

be used to determine the compaction.

(b)	Testing

Field moisture-density tests using acceptable methods shall be required at random

locations at the rate of each 250 lineal feet of paving for each travel lane.

TABLE 500-4

MOISTURE-DENSITY CONTROL

AASHTO T 99	AASHTO T 180

Minimum Relative	Minimum Relative

Soil Classification	Compaction	Compaction

(AASHTO M 145)	Percent	Percent

A-1		100	95

A-3		100	95

A-2-4	100	95

A-2-5	100	95

All Other	95	90

(c)	Final Proof-Rolling

After the subgrade has been compacted, tested and found to meet specifications, the

entire subgrade shall be proof-rolled with a heavily loaded vehicle. The vehicle

must have a certified loaded single axle weight of at least 18,000 pounds and a tire

pressure of 90 psi. Subgrade which is pumping or deforming must be reworked,

replaced or otherwise modified to form a smooth, stable, non-yielding base of

subsequent paving courses. The City Engineer shall be notified at least 48 hours

before final proof-rolling.

(d)	Acceptance

The results of field density tests and proof-rolling shall be submitted and reviewed

by the City Engineer. Provided all tests are acceptable, compaction shall be

approved for the placement of next paving course. Should testing indicate

unsatisfactory work, the necessary reworking, compaction or replacement shall be

required prior to continuation of the paving process. The approval is valid for 24

hours. Changes in weather, such as freezing or precipitation, shall require

reapproval of the subgrade.

508.5	Lime Treated Subgrade

(a)	Materials

Lime treated subgrade shall be used only where a mix design has been previously

submitted and approved by the City Engineer.

508.6	Aggregate Base Course

(a)	Materials

Aggregate base course materials must be from a currently approved source. The

Responsible Party shall, upon request, provide verification of material properties.

(b)	Placement and Compaction

Materials shall be placed on an approved subgrade which has been proof-rolled within

the past 24 hours and found to be stable and non-yielding. Should weather conditions

change, such as freezing, precipitation, etc., aggregate base materials shall not be

placed until the subgrade is reapproved.

Aggregate base materials shall be placed, moisture treated and compacted as outlined

in Section 305 of the NDOR Standard Specifications.

(c)	Testing

At least one sample of aggregate base course for each 1,000 tons of material placed

shall be tested to determine gradation and Atterberg limits. Should these tests

indicate the material does not meet specifications, the material shall be removed

and replaced.

During placement and compaction, Compaction Curves shall be required for each

material used. Field moisture-density tests shall be taken of each lift of material

at random locations, at approximate intervals of 250 feet in each travel lane. At

least 20 percent of the tests shall be taken within one foot of manholes, valves

and curbs.

(d)	Approval

The results of field density tests shall be submitted and reviewed by the City

Engineer provided all tests are acceptable, the aggregate base course materials,

placement and compaction shall be approved and the next paving course can be

placed. Should testing indicate unsatisfactory work, the necessary reworking,

compaction or replacement shall be required prior to continuation of the paving

process.

508.7	Plant Mix Bituminous Pavement

(a)	Materials

All asphalt, aggregate, fillers and additives shall be combined to form a mix

design. The mix design must be submitted to and approved by the City Engineer.

(b)	Placement and Compaction

Materials shall be placed upon an approved subgrade or previous paving course in

accordance with Section 507 of the NDOR Standard Specifications. Prime or tack coats

shall be applied in accordance with subsection 504.4 of these Standards and

Specifications.

When more than one lift of pavement is required, the joints or seams between lifts

shall be staggered so that joints are separated by at least two feet in the

horizontal direction. Joints in the final wearing course shall not be located in

probable wheel paths.

The bituminous paving mix shall be compacted to at least 95 percent of the mix

determined Marshall density or specified density from Hveem testing to achieve

design strength.

(c)	Testing

During placement and compaction of plant-mix bituminous pavement, observation and

testing shall be on a full-time basis at the expense of the Responsible Party. For

each day of production or each 1,000 tons of material placed a field sample shall

be taken and subjected to Marshall or Hveem testing, extraction and gradation

analysis. The results shall be used to control compaction in the field.

Mix temperatures shall be checked on each truck. Where the temperature does not meet

specifications, the load shall not be placed and shall be removed from the site

entirely.

During compaction, the density of the pavement shall be checked randomly at the

rate of one test for each 250 lineal feet of travel for each lift. Nuclear test

methods are suggested.

Either during or after completion of the paving, the final pavement thickness shall

be determined for the plant mix bituminous pavement using coring, rings or other

acceptable methods. Thickness determination shall be made at random locations at

intervals of approximately 250 feet in each travel lane.

(d)	Approval

The results of field density and laboratory tests shall be submitted and reviewed

by the City Engineer. Provided all tests are acceptable, the asphaltic concrete

materials, placement and compaction shall be approved. Acceptable results shall

be compliance with tolerances for gradation and extraction. Marshall stability

test results shall average 1,500 lbs. or more. Should testing indicate

unsatisfactory work, removal and replacement or overlay work shall be required.

Criteria used to determine satisfactory work shall be all of the following and be

in compliance with the Pavement Evaluation Report:

1.	Ninety percent of core tests must meet or exceed design HBP thickness;

2.	Average of all core tests must meet or exceed design HBP thickness;

3.	All core test thicknesses must exceed design HBP thickness minus 1/2 inch.

508.8	Portland Cement Concrete

(a)	Materials

All aggregate, Portland cement, fly ash, water, admixtures, curing materials and

reinforcing steel shall be combined into a mix design and submitted to, and

approved by, the City Engineer.

(b)	Construction Requirements

Materials shall be proportioned, handled, measured, batched, placed and cured in

accordance with Section 601 of NDOR Standard Specifications.

(c)	Testing

(d)	Placement

During placement of Portland cement concrete pavement, observation and testing shall

be on a full-time basis. For each day of production or 1,000 square yards placed,

aggregate samples shall be obtained for gradation of both the coarse and fine

aggregates.

(e)	Interval

Slump, air content, unit weight and mix temperatures shall be tested three times for

every 1,000 square yards of pavement placed. All tests for slump and air content

shall be on a random basis.

(f)	Cylinders

Four compressive strength cylinders shall be fabricated for each 1,000 square yards

placed. Cylinders shall be tested as follows:

two at seven days

two at 28 days

(g)	Fly Ash

Portland cement and fly ash shall be accepted on the basis of certificates of

compliance and pretesting by NDOR and subject to approval of the City Engineer.

Reinforcing steel, dowels and tie bars shall be accepted by certificate of

compliance and mill reports. Only NDOR approved brands of air entraining agents,

chemical admixtures and curing materials may be used and must be documented.

(h)	Thickness Check

Thickness of fresh concrete must be checked every three hundred (300) lineal feet in

each traffic lane. Any noted deficient areas shall be corrected at that time.

Surface smoothness shall be tested and corrected as necessary according to NDOR

Standard Specifications, Section 601.

(i)	Approval

All test results shall be submitted and reviewed by the City Engineer. Provided all

tests are acceptable, the pavement shall be accepted. Should testing indicate

unsatisfactory work, removal and replacement or grinding shall be required.

508.9	Asphalt Prime and Tack Coats

(a)	Materials

Emulsified asphalt of any of the following grades may be used:

SS-1

SS-1h

CSS-1

CSS-1h

All of these should be diluted 1:1 with water. A certificate of compliance must be

provided by the supplier.

(b)	Application

Prior to prime coat application, the surface should be allowed to dry to

approximately 80 percent of optimum moisture. The asphalt material shall be applied

in the range of 0.20 to 0.40 gallons/square yards.

Tack coat shall be applied where additional HBP is to be placed over existing

asphaltic or Portland cement surfaces. Tack coats shall not be required where HBP

is less than 24 hours old and remains free of dust, dirt or debris. A 1:1 dilution

should be applied at 0.10 gallon per square yard should be used for a tack coat on

existing pavement. A wand, or hand spray nozzle attached to the spray bar can be

used for applying tack to gutter faces, valve boxes, manholes and rings.

(c)	Curing

Curing shall be required for all prime and tack coats. The prime or tack coat shall

be sticky, or tacky, when cured. The length of time required for curing shall

depend on the air temperature, humidity and wind conditions and shall be black when

cured.

(d)	Approval

Prime or tack coat shall be approved by the City Engineer upon acceptance of mill

certifications, visual approval and verification of application rate. Dust or

contamination of prime or tack coats shall require brooming and reapplication.

508.10	Geotextile Fabric

(a)	Fabric

All geotextile fabric shall meet pavement design report criteria and subject to the

approval of the City Engineer.

SECTION 600

CONCRETE WORK

SECTION 600 - CONCRETE WORK

TABLE OF CONTENTS			PAGE

601	GENERAL PROVISIONS		600-1

602	MATERIALS				600-1

602.1	Cement			600-1

602.2	Water			600-1

602.3	Admixtures		600-1

602.4	Fine Aggregate		600-2

602.5	Coarse Aggregate		600-2

602.6	Fibrous Reinforcing		600-2

603	MIXING					600-3

603.1	General			600-3

603.2	Design of the Mix		600-4

603.3	Ready-Mixed Concrete		600-4

604	REINFORCING STEEL AND FORMS		600-4

605	PLACING CONCRETE			600-6

605.1	Vibrating			600-6

605.2	Workability		600-6

606	JOINTS					600-7

606.1	Materials			600-7

606.2	Spacing			600-7

607	FINISHING AND CURING		600-8

608	PROTECTION				600-9

608.1	Cold Weather Concreting		600-9

608.2	Hot Weather Concreting		600-10

609	MISCELLANEOUS			600-10

609.1	Repairs			600-10

609.2	Cleanup			600-11

609.3	Backfilling		600-11

609.4	Testing			600-11

610	FLOWCRETE / FLOWFILL CONCRETE		600-13

610.1	Specifications		600-13

SECTION 600 - CONCRETE WORK

601	GENERAL PROVISIONS

All concrete work within any street, park, trail or alley rights-of-way or in any part of the

water system, sewage system, parks, and storm drainage system of the City shall meet the

requirements of these Standards and Specifications. Engineering, plans, licenses, permits,

inspection, warranties and acceptance shall be as detailed in these applicable Standards and

Specifications for the type of construction involved.

Permits shall be obtained before work begins. Responsible Party shall give the City Engineer

48 hours notice, and inspection shall be made before placement of concrete can occur. Written

notice of Inspector's approval to place materials shall be obtained by Responsible Party after

inspection has been made and before concrete is placed. Written notice of rejection shall be

given to Responsible Party in the event any aforementioned conditions given by the City Engineer

are not met, and work shall be halted until such time as corrective action is taken. Copies of

the approved drawings and the permit shall be on the job site and available to the Inspector.

602	MATERIALS

Concrete shall be composed of Portland Cement, aggregate, and water, and shall be reinforced

with steel bars, steel wire fabric or fibrous reinforcing where required. No admixture other

than air-entraining agents shall be used without written permission by the City Engineer.

602.1	Cement

All cement used in concrete work shall be Portland Cement conforming to the requirements

of ASTM C-150. In general, Type I or II or I, IILA shall be used in concrete which shall

be in contact with the soil, unless otherwise allowed or directed by the City Engineer.

Cement, which for any reason has become partially set or which contains lumps or caked

cement, shall be rejected.

The Responsible Party shall be responsible for the proper storage of all cement until it

is used. No damaged cement shall be used in the work, and all such cement shall be

immediately removed from the site when so ordered by the City Engineer. When requested

by the City engineer, the Responsible Party shall, at his own cost and expense, furnish

the City Engineer with a certificate from an acceptable testing laboratory for each

carload of cement from which cement is taken for use in the work, stating that the

cement meets the requirements of these Standards and Specifications for Portland Cement.

602.2	Water

Water for concrete shall be clean and free from sand, oil, acid, alkali, organic matter,

or other deleterious substances. Water from public supplies or water which has been

proven to be suitable for drinking is satisfactory.

602.3	Admixtures

The Responsible Party shall use air-entraining admixtures for all surfaces of exposed

concrete. The Responsible Party may elect to use another admixture provided the admixture

is specifically approved by the City Engineer. Admixtures to be used for plasticizing,

densifying, or acceleration of hardening of concrete shall, when added to the mixture,

produce a concrete of specified strength in seven day, 14 day, and 28 day tests.

Documented evidence of acceptability shall be required when new or unknown admixtures

are proposed for use. Air-entraining admixtures shall conform to the requirement of

ASTM C-260.

602.4	Fine Aggregate

Fine aggregate shall be composed of clean, hard, durable, uncoated particles of sand,

free from injurious amounts of clay, dust, soft or flaky particles, loam, shale, alkali,

organic matter, or other deleterious matter. Fine aggregate shall be well graded from

coarse to fine and when tested by means of laboratory sieves shall meet the Nebraska

Department of Roads Concrete Aggregate Gradation Table 1015.01 and also conform to AASHTO

M6.

Sieve Size                     Percent Passing

3/8"		100

#4		77-97

#10		50-70

#30		16-40

#100		0-3

602.5	Coarse Aggregate

The coarse aggregate shall consist of broken stone or gravel composed of clean, hard,

tough and durable stone and shall be free from soft, thin, elongated or laminated pieces,

disintegrated stone, clay, loam, organic, or other deleterious matter.

Coarse aggregate shall conform to the NDOR Concrete Aggregate Gradation Table 1015.02

which shall also conform to AASHTO M43.

602.6	Fibrous Reinforcing

(a)	Fibrous reinforcing may be used in Portland Cement concrete to prevent surface

shrinkage cracking.

(b)	The following shall be submitted to the City Engineer:

1.	One copy of manufacturer's printed product data, clearly marked, indicating

proposed fibrous concrete reinforcement materials. Printed data should state

1.5 lbs. of fiber to be added to each cubic yard of each type of concrete.

2.	One copy of manufacturer's printed batching and mixing instructions.

3.	On copy of a certificate prepared by the concrete supplier stating that the

approved fibrous concrete reinforcement materials at the rate of 1.5 lbs.

per cubic yard were added to each batch of concrete delivered to the project

site. Each certificate shall be accompanied by one copy of each batch delivery

ticket indicating amount of fibrous concrete reinforcement material added to

each batch of concrete.

(c)	Fibrous concrete reinforcement shall consist of:

1.	One hundred percent virgin polypropylene fibrillated fibers specifically

manufactured for use as concrete reinforcement, containing no reprocessed

olefin materials. Fibrous concrete reinforcement shall be as manufactured

by Fibermesh Company, 4019 Industry Drive, Chattanooga, Tennessee, 37416,

or approved equivalent. Substitutions may be considered at the discretion

of the City.

2.	Physical characteristics:

(a)    Specific gravity = 0.905 grams per cubic centimeter.

(b)    Tensile strength: 70 to 110.

(c)    Fiber lengths: 1/2", 3/4", 1-1/2", 2" per manufacturer.

(d)    Fibrous concrete reinforcement materials provided by this subsection

shall produce concrete conforming to the requirements for each type

and class of concrete required as indicated.

(e)    Construction methods

1.  Add fibrous concrete reinforcement to concrete materials at the time

concrete is batched in amounts in accord with approved submittals

for each type of concrete required.

2.  Mix batched concrete in strict accord with fibrous concrete

reinforcement manufacturer's instruction and recommendations for

uniform and complete dispersion.

(f)    Concrete placing and finishing. Place and finish concrete materials as

specified in subsection 605 and 607.

603	MIXING

603.1	General

All concrete shall be thoroughly mixed in a batch mixer of an approved type and capacity

for a period of not less than two minutes after all the materials, including the water,

have been placed in the drum. During the period of mixing, the drum shall be operated at

the speed specified by the manufacturer of the equipment. The entire contents of the

mixer shall be discharged before recharge, and the mixer shall be cleaned frequently. The

concrete shall be mixed only in such quantities that are required for immediate use. No

retempering of concrete shall be permitted. Hand-mixed concrete shall not be permitted

except by written approval of the City Engineer, and then in only very small quantities

or in case of an emergency.

603.2	Design of the Mix

(a)	Proportioning

Proportioning the "dry" constituents of all concrete mixtures shall be accomplished

by weighing. The Responsible Party shall provide adequate and accurate scales for

this work. Scales shall be accurate within the allowable tolerances as prescribed

by state law. The scales shall be sealed by the measurement standards section of

the Nebraska Department of Agriculture at least once each year, each time the

scales are relocated, and as often as the engineer may deem necessary. Scales

shall be operated by weighers certified by the measurement standards section of

the Nebraska Department of Agriculture. The certified weigher shall perform the

duties according to the Nebraska Department of Agriculture's regulations. There

shall be no variance permitted in the minimum cement factor (sacks per cubic

yard) as specified for the calls of concrete. The total quantity of mixing-water

per sack of cement, including free water in the aggregates, shall not exceed the

maximum specified herein. The Responsible Party shall be responsible for developing

the proper proportions of aggregates, cement and water that shall conform to the

various requirements of these Standards and Specifications. Mix design shall be

submitted to the City Engineer, along with at least two sets of certified 28 day

test results, for review and approval. No concrete shall be incorporated into

the work until the proportions are approved by the City Engineer.

603.3	Ready-Mixed Concrete

The use of ready-mixed concrete in no way relieves the Responsible Party of the

responsibility for proportion, mix, delivery, or placement of concrete; all concrete

must conform to all requirements of these Standards and Specifications and ASTM C-94.

Concrete shall be continuously mixed or agitated from the time the water is added until

the time of use and shall be completely discharged from the truck mixer or truck agitator

within 1-1/2 hours after it comes in contact with the mixing water or with the aggregate.

Retempered concrete shall not be allowed.

The City shall have free access to the mixing plant at all times of operation. The

organization supplying the concrete shall have sufficient plant and transportation

facilities to assure continuous delivery of the concrete at the required rate. (The

Responsible Party shall collect delivery, or batch, tickets from the driver for all

concrete used on the project and deliver them to the City Engineer). Batch tickets shall

provide the following information: 1.) weight and type of cement; 2.) weights of fine

and coarse aggregates; 3.) volume (in gallons) of water including surface water on

aggregates; 4.) quantity (cubic yards) per batch; 5.) times of batching and discharging

of concrete; 6.) name of batch plant; 7.) name of Responsible party; 8.) type; 9.) name

and amount of admixture; and 10.) date and truck number.

604	REINFORCING STEEL AND FORMS

Before being positioned, all reinforcing steel shall be thoroughly cleaned of mill and rust

scale and of coating that shall destroy or reduce the bond. Where there is delay in depositing

concrete, reinforcement shall be reinspected and, if necessary, cleaned.

Reinforcement shall be carefully formed to the dimensions indicated on the plans by the cold

bending method. Cold bends shall be made around a pin having a diameter of six or more times

the diameter of the reinforcing bars. Reinforcement shall not be bent then straightened. Bars

with kinks or bends not shown on the plans shall not be used. Precast mortar blocks, or other

non metal supports not approved by ACI shall not be allowed to remain in the concrete

placement.

Reinforcing steel shall be accurately placed and secured against displacement by using

annealed iron wire of not less than No. 18 gauge, or by suitable clips at intersections.

Where necessary, reinforcing steel shall be supported by metal chairs or spacers, precast mortar

blocks, or metal hangers. Splicing of bars, except where shown on the plans, shall not be

permitted without approval of the City Engineer.

Welded wire fabric for concrete reinforcement shall be of the gauge, spacing, dimensions, and

form specified on the plans or detailed drawings and shall comply with "Specifications for

Welded Steel Wire Fabric for Concrete Reinforcement" (ASTM A-741) or "Specification for Welded

Deformed Steel Wire Fabric for Concrete Reinforcement" (ASTM A-497).

Responsible Party shall submit to the City Engineer shop drawings of the reinforcement for his

approval. The City Engineer's approval of shop drawings and bar schedules shall not relieve the

Responsible Party of fulfilling his responsibilities as outlined in the plans and

specifications.

Unless otherwise shown on the plans, the minimum clear cover for reinforcing steel shall be the

following, which is specified in ACI 310, Sec. 5.5:

o Bottom bars on soil bearing foundations and slabs, 3 inches

o Bars adjacent to exposed surfaces or earth backfill:

For bars more than 3/4 inch in diameter, 2 inches

For bars 3/4 inch or less in diameter, 1-1/2 inches

o Interior Surfaces: slabs, walls, joints with 1-3/8 inch diameter or smaller, 3/4 inches

Whenever necessary, forms shall be used to confine the concrete and shape it to the required

lines. Forms shall have sufficient strength to withstand, without deformation, the pressure

resulting from placement and vibration of the concrete. Forms shall be constructed so that the

finished concrete shall conform to the shapes, lines, grades and dimensions indicated on the

approved plans. Any form which is not clean and has not had the surface prepared with a

commercial form oil that shall effectively prevent bonding and that shall not stain or soften

concrete surface shall not used.

Plywood forms, plastic coated plywood forms, or steel forms shall be used for all surfaces

requiring forming which are exposed to view, whether inside or outside any structure. Surfaces

against backfilled earth, interior surfaces of covered channels, or other places permanently

obscured from view, may be formed with forms having sub-standard surfaces.

Forms shall not be disturbed until the concrete has hardened sufficiently to permit their

removal without damaging the concrete or until the forms are not required to protect the

concrete from mechanical damage. Minimum time before removal of forms after placing concrete

shall be one day for footings and two days for all other concrete except in curbs, gutters,

sidewalks and pavements. The use of slip forms and concrete paving machines shall be allowed,

with approval of the City Engineer.

605	PLACING CONCRETE

The subgrade shall be excavated or filled to the required grades and lines. All soft, yielding,

or otherwise unsuitable material shall be removed and replaced with suitable material. Filled

sections shall be compacted and compaction shall extend a minimum of one foot outside the form

lines.

The subgrade shall be compacted to the density shown on the plans and trimmed to provide a

uniform surface at the correct elevation.

Before depositing concrete, debris shall be removed from the space to be occupied by the

concrete and the forms, including any existing concrete surfaces, shall be thoroughly wetted.

Concrete shall not be placed until all forms and reinforcing steel have been inspected and

approved by the City Engineer. Concrete shall be handled from the mixer to the place of final

deposit as rapidly as possible by methods which prevent separation or loss of ingredients. The

concrete shall be deposited in the forms as nearly as practicable in its final position to

avoid rehandling. It shall be deposited in continuous layers, the thickness of which generally

shall not exceed 12 inches. Concrete shall be placed in a manner that shall avoid segregation

and shall not be dropped freely more than five feet. If segregation occurs, the City Engineer

may require the concrete to be removed and replaced at the Responsible Party's expense.

Concrete shall be placed in one continuous operation, except where keyed construction joints

are shown on the plans or as approved by the City Engineer. Delays in excess of 30 minutes may

require removal and replacement of that pour, as determined by the City Engineer.

605.1	Vibrating

Concrete shall be thoroughly compacted and/or vibrated. All concrete shall be compacted

by internal vibration using mechanical vibrating equipment, except that concrete in

floor slabs, sidewalks, or curb and gutter, not poured against form linings, shall be

either tamped or vibrated. Care shall be taken in vibrating the concrete to vibrate

only long enough to bring a continuous film of mortar to the surface. Vibration shall

stop before any segregation of the concrete occurs. Mechanical vibrators shall be an

approved type as specified in ACI Publication 309, Chapter 5. Vibrators shall not be

used to move or spread the concrete.

Any evidence of the lack on consolidation or overconsolidation shall be regarded as

sufficient reason to require the removal of the section involved and its replacement

with new concrete at the Responsible Party's expense. The Responsible Party shall be

responsible for any defects in the quality and appearance of the completed work.

605.2	Workability

The consistency of concrete shall be kept uniform for each class of work and shall

be checked by means of slump tests or Kelly ball tests. The workability of the concrete

shall be varied as directed by the City Engineer. At all times concrete shall have a

consistency such that it can be worked into corners and angles of the forms and around

joints, dowels and tie-bars by the construction methods which are being used without

excessive spading, segregation or undue accumulation of water or latent material on the

surface. If, through accident, intention, or error in mixing, any concrete fails to

conform to the proportions of the approved mix design, such concrete shall not be

incorporated in the work but shall be properly disposed of off the project site as

waste material at the Responsible Party's expense. No water may be added at the job

site without permission of the City Engineer. If approval is obtained and water is

added at the job site, slump tests shall be run and test cylinders cast following the

addition of the water. Any expense incurred in excess of ordinary tests shall be

borne by the Responsible Party.

606	JOINTS

606.1	Materials

Joint materials shall conform to AASHTO, ASTN Specifications according to type as

follows:

AASHTO        	ASTN

Concrete joint sealer, hot poured elastic or 	M 173          D1190-74

approved Cold Pour or an approved equivalent

Performed expansion joint filler (Bituminous Type)	M 33           D994-71

Preformed sponge rubber and cork expansion	M 153          D1752-67

joint fillers

Preformed expansion joint fillers		M 213          D1751-73

nonextruding and resilient bitumen

606.2	Spacing

(a)	Expansion Joints

Expansion joint material shall be provided at the following locations and shall be

in place prior to the placing of concrete:

1.	At each end of curb return.

2.	At both edges of driveway.

3.	Between back of sidewalk and driveway slab or service walk.

4.	Between new concrete and existing masonry buildings.

5.	As shown on the drawings.

6.	As directed by the City Engineer.

7.	Between new and existing concrete.

8.	Every 100 feet in sidewalk, curb and gutter when handformed.

9.	Every 200 feet in sidewalk, curb and gutter when placed slip formed.

10.	Inlets

(b)	Contraction Joints

Transverse joints shall be placed at maximum intervals not to exceed twice the

spacing, in feet, of the thickness in inches, to control random cracking; joints

shall be formed, sawed, or tooled to a minimum depth of 1/4 of the total thickness.

If divider plates are used, the maximum depth of plates shall not be greater than

one-half depth at the finished surface and shall be no less than 15/16 inch.

(c)	Tool Joints

Tool joints shall be spaced as follows:

1.	Not more than 10 feet nor less than five feet apart in curb and gutter and

combination curb-walk.

2.	Not more than the width of the sidewalk (up to eight feet), nor less than five

feet apart in sidewalk.

3.	At least two joints, equally spaced at not greater than 10 foot intervals as

applicable in driveways.

4.	As directed by the City Engineer.

607	FINISHING AND CURING

Exposed faces of curbs and sidewalks shall be finished to true-line and grade as shown on the

plans. Surface shall be floated to a smooth but not slippery finish. Sidewalk and curb shall

be broomed or combed and edged, unless otherwise directed by the City Engineer. After completion

of brooming and before concrete has taken its initial set, all edges in contact with the forms

shall be tooled with an edge having a 3/8 inch radius. No dusting or topping of the surface or

sprinkling with water to facilitate finishing shall be permitted.

Immediately following the removal of the forms, all fins and irregular projections shall be

removed from all surfaces except from those which are not to be exposed or are not to be

waterproofed. On all surfaces, the cavities produced by form ties, honeycomb spots, broken

corners or edges, and other defects, shall be thoroughly cleaned, moistened with water and

carefully pointed and trued with a mortar consisting of cement and fine aggregate. The surface

shall be left sound, of acceptable finish, even, and uniform in color. Mortar used in pointing

shall not be more than 30 minutes old. All construction and expansion joints in the completed

work shall be left carefully tooled and free of all mortar and concrete. The joint filler shall

be left exposed for its full length with clean and true edges. Any surface determined to be not

acceptable by the City Engineer shall be removed and replaced by the Responsible Party, at no

expense to the City.

Fresh concrete shall be adequately protected from weather damage and mechanical injury during

the curing periods. Curing processes described herein may be used at the option of the City

Engineer. The selected curing process shall be started as soon as it can be done without injury

to the concrete surface. The use of a membrane curing compound is required.

The following curing procedures may be used subject to the approval of the City Engineer:

1.	Ponding (for slabs or footings)

2.	Spraying

3.	Wet burlap, earth, or cotton mats

4.	Waterproof paper or polyethylene plastic cover

Membrane curing compound shall not be used when the concrete surface shall be painted. The type

of membrane curing compound shown shall not permanently discolor the concrete surface. Where

membrane curing compound is not used, the curing process shall be carefully adhered to as

follows:

1.	Surfaces being wetted by ponding, spraying, or wetted material shall be kept

completely wetted, with an excess of free water on the surface, at all times for the

first 72 hours. After this period, but for the remaining four days, a wetting

schedule shall be followed whereby the concrete is wetted on a schedule approved by

the City Engineer.

2.	Surfaces being protected by waterproof paper or polyethylene plastic cover shall

receive special attention during the first 72 hours to insure there is actually free

moisture on the surface of the concrete under the waterproof surface. The engineer

may require the removal of the cover and a wetting of the surface when, in his

judgement, there is insufficient moisture for curing. After the first 72 hours the

cover shall be kept tightly in place for the remainder of the curing period.

608	PROTECTION

608.1	Cold Weather Concreting

During extreme weather conditions, placing of concrete shall be permitted only when the

temperature of the concrete placed in the forms shall not be less than 60 degrees F, nor

more than 90 degrees F. To maintain this temperature range, the Responsible Party shall

provide acceptable heating apparatus for heating the aggregates and the water. Concrete

may be placed when the air temperature in the shade is 40 degrees F, and rising. No

concrete shall be placed, regardless of the present temperature, when the weather

forecast promises freezing weather before final set of the concrete unless special means

of heating and protection are used. Protection against freezing is the Responsible

Party's responsibility regardless of the weather forecast or climatic conditions at the

time of placing.

Small structures and slabs may be protected by completely covering fresh concrete with

dry straw and canvas to a depth that insures protection. Material shall be secured to

prevent displacement by the elements. Large structures or vertical walls shall be

protected against freezing by enclosing the structure and heating with salamanders,

heaters, or other devices capable of providing uniform and even heat throughout the

structure.

Concrete placed in cold weather shall be protected from extreme temperatures as follows:

1.	A temperature of at least 50 degrees F for the first 72 hours shall be maintained.

2.	After the first 72 hours and until the concrete is seven days old, it shall be

protected from freezing temperatures.

3.	Concrete adjacent to heaters or salamanders shall be insulated from direct heat

of the unit which may dry it out prior to being properly cured.

4.	Temperatures shall be measured by maximum and minimum thermometers, furnished by

the Responsible Party and installed adjacent to the concrete.

Concrete slabs shall not be placed, regardless of temperature conditions, if the

supporting ground is frozen or contains frost. Use of salt or other additives to

prevent concrete from freezing shall not be allowed. Concrete which has been frozen

shall be completely removed and replaced as directed by, and to the satisfaction of,

the City Engineer.

608.2	Hot Weather Concreting

Except by written authorization, concrete shall not be placed if the temperature of the

plastic concrete cannot be maintained at 90 degrees F, or lower. The placement of

concrete in hot weather shall comply with ACI 305.

609	MISCELLANEOUS

609.1	Repairs

After stripping of the forms, if any concrete is found to be not formed as shown on the

drawings or is out of alignment or level, or shows a defective surface, it shall be

considered as not conforming with the intent of these Standards and Specifications and

shall be removed and replaced by the Responsible Party at his expense unless the City

Engineer gives written permission to patch the defective are. In this case, patching

shall be done as described in the following paragraphs. Defects that require replacement

or repair are those that contain honeycomb, damage due to stripping of forms, loose

pieces of concrete, bolt-holes, tie-rod holes, uneven or excessive ridges at form

joints, and bulges due to movement of the forms. Ridges and bulges shall be removed by

grinding. Honeycombed and other defective concrete that does not affect the integrity of

the structure shall be chipped out, and the vacated areas shall be filled in a manner

acceptable to the City Engineer. The repaired area shall be patched with a non-shrink,

non-metallic grout with a minimum compressive strength of 5,000 psi in 28 days. All

repair areas treated with an epoxy bonding agent shall have the approval of the City

Engineer before the repair filling is placed.

Bolt-holes, tie-rod holes, and minor imperfections as approved by the City Engineer,

shall be filled with dry-patching mortar composed of one part Portland cement to two

parts of regular concrete sand (volume measurement) and only enough water so that

after the ingredients are mixed thoroughly, the mortar shall stick together on being

molded. Mortar repairs shall be placed in layers and thoroughly compacted by suitable

tools. Care shall be taken in filling rod and bolt holes that the entire depth of the

hole is completely filled with compacted mortar. The mortar mix proportions described

above are approximate.

Those areas with excessive deficiencies as determined by the City Engineer shall be

removed and replaced at the Responsible Party's expense. Where repairs are made in

existing sidewalks, all edges of the old sidewalk allowed to remain shall be sawcut to

a minimum depth of two inches. No rough edges shall be permitted where new construction

joins the old section. Unless directed by the City Engineer, no section less than five

feet in length shall be placed or left in place. Where new sidewalk construction abuts

existing sidewalks, the work shall be accomplished so that there is no abrupt change

in grade between the old section and the new work.

No addition to existing sidewalks or other flat work concrete shall be made less than 4

feet in width. Doweling into the existing concrete may be required by the City Engineer.

609.2	Cleanup

The exposed surfaces of the concrete shall be thoroughly cleaned upon completion of the

work, and the site shall be left in a neat and orderly condition.

609.3	Backfilling

When side forms are removed and the concrete has gained sufficient strength, the space

adjoining the concrete shall be promptly backfilled with suitable material, properly

compacted, and brought flush with the surface of the concrete and adjoining ground

surface. In embankments, the backfill shall be level with the top of the concrete for

at least two feet and then sloped as shown on the drawings or as directed by the City

Engineer.

When the area behind the walk is to be paved, a minimum of four inches of asphaltic

surfacing shall be used and shall be constructed in accordance with these Standards and

Specifications. Existing pavement which is damaged during construction shall be repaired

by the Responsible Party at his expense. The first two feet of patching to match existing

asphalt or concrete shall be the Responsible Party's responsibility.

609.4	Testing

(a)	General

The requirements of this section shall apply to testing services for all concrete

curb and gutter, sidewalk, pavement, slope paving, retaining walls, structures, and

for all miscellaneous concrete testing.

Concrete materials and operations shall be tested as directed by the City Engineer

and as herein stipulated. The required testing services shall be performed by a

testing agency approved by the City Engineer and all testing agencies shall meet the

requirements of ASTM E329.

A representative of the testing agency shall inspect, sample, and test material and

production of concrete as required by the City Engineer at the Responsible Party's

expense. When it appears that any material furnished or work performed by the

Responsible Party fails to fulfill specification requirements, the testing agency

shall report such deficiency to the City Engineer and the Responsible Party.

The testing agency shall report all test and inspection results to the City Engineer

and Responsible Party immediately after they are performed. All test reports shall

include the exact location of the work at which the batch represented by a test was

deposited. The report of the strength test shall include detailed information on

storage and curing of specimen prior to testing, the project number, and the

location of the concrete (curb, manhole, inlet, sidewalk, pacing, etc.). All test

reports shall bear the seal and signature of a professional Engineer registered in

the state of Nebraska and competent in the field of concrete testing. Reports not

properly certified shall shall not be accepted.

The testing agency or its representative is not authorized to revoke, alter, relax,

enlarge or release any requirements of these Standards and Specifications, nor

approve or accept any portion of the work.

(b)	Tests Provided by the Responsible Party

The following services shall be performed by the designated testing agency at the

expense of the Responsible Party:

1.	Conduct strength test of the concrete during construction in accordance with

the following procedure: Secure composite samples in accordance with AASHTO

T141; mold and cure specimens from each sample in accordance with AASHTO T23.

The maximum time between sampling and casting the cylinders or beams shall be

45 minutes. One test series shall be taken per 50 cubic yards (or fraction

thereof) of the concrete placed per day, or as directed by the City Engineer.

a.    Lab cured test series: four cylinders, two to be broken at seven days;

two to be broken at 28 days.

2.	Determine slump of the concrete sample of each strength test whenever

consistency of concrete appears to vary, or when directed by the City Engineer,

in accordance with AASHTO T119.

3.	Determine air content of the concrete sample for each strength test in

accordance with either AASHTO T152 (pressure method), T196 (volumetric method),

or T121 (gravimetric method).

4.	Sample additional concrete at point of placement, and perform other testing or

inspection service as required.

5.	When required by the City Engineer, the Responsible Party shall provide

concrete mix designs, the results of which shall be immediately reported to

the City Engineer. When pumped concrete is to be used, a separate mix design

shall be required. Mix designs shall be in accordance with ACI 211 and 304,

as applicable.

6.	Additional testing and inspection required because of changes in materials or

proportions.

7.	When the work fails to pass inspection or previous tests fail to meet

specifications, additional tests shall be taken as directed by the City

Engineer.

8.	Core samples shall be obtained and tested when samples of fresh concrete were

not obtained and tested in accordance with the provisions of these Standards

and Specifications. Obtaining and testing cores shall be in accordance with

ASTM C42. Concrete in the area represented by a core test shall be considered

adequate if the average strength of the cores is equal to at least 85 percent

of the specified strength, and if no single core is less than 75 percent of

the specified strength. Core holes shall be filled with low slump concrete or

mortar.

9.	Failure of the Responsible Party to furnish testing as herein described shall

be sufficient cause for rejection of the work in question.

(c)	Responsibility of Duties of the Responsible Party

The Responsible Party shall provide the testing agency with the following:

1.	Any labor necessary to assist the designated testing agency in obtaining and

handling samples at the project or from other sources of material.

2.	Provide and maintain for the sole use of the testing agency adequate facilities

for safe storage and proper curing of concrete test specimens on the project

site as required by AASHTO T23.

The use of testing services in no way relieves the Responsible Party of the

responsibility to furnish material and construct in full compliance with these

Standards and Specifications.

610	FLOWCRETE / FLOWFILL CONCRETE

610.1	Specifications

The following is the specification of the flowcrete/flowfill concrete as directed by

the City Engineer.

Mix Properties: (per cubic yard of concrete)

Material               ASTM Specification               Weight

Cement                 ASTM C-150                       42 to 50 lbs.

Sand                   ASTM C-33                        1845 to 1850 lbs.

Aggregate              ASTM C-33                        1700 to 1750 lbs.

Air Entrainment        ASTM C-260                       5.0 ounces

Water                  ASTM C-94                        39 gallons

DESIGN PHYSICAL PROPERTIES:    Slump shall be 6 to 8 inches

SECTION 700

TRAFFIC SIGNAL

TECHNICAL SPECIFICATIONS

SECTION 700 - TRAFFIC SIGNAL TECHNICAL SPECIFICATIONS

TABLE OF CONTENTS			PAGE

701	GENERAL				700-1

702	TRAFFIC SIGNAL CONTROLLER ASSEMBLY		700-1

702.1	General Design Requirements		700-1

702.2	Functional Operation		700-2

702.3	Displays and Keyboard		700-4

702.4	Time Clock		700-4

702.5	Coordination		700-6

702.6	Preemption		700-6

702.7	Miscellaneous Features		700-7

702.8	Conflict Monitor		700-7

702.9	Loop Detector Amplified		700-8

702.10	Cabinet			700-9

703	TRAFFIC SIGNALIZATION SYSTEM		700-10

703.1	General			700-10

703.2	Pole Design		700-10

703.3	Mast Arm Design		700-11

703.4	General Signalization		700-11

704	TRAFFIC POLE FOUNDATION SPECIFICATIONS		700-12

704.1	General			700-12

704.2	Reinforcing Steel		700-12

704.3	Ground Rod 		700-12

704.4	Anchor Bolts		700-13

704.5	Conduit Bends		700-13

704.6	Spare Bend		700-13

704.7	Concrete			700-13

705	TRAFFIC DETECTION LOOPS		700-13

706	STREET NAME SIGN			700-14

706.1	General			700-14

707	EMERGENCY VEHICLE PREEMPTION SYSTEM		700-14

707.1	System Description		700-14

707.2	Detailed Requirements		700-14

708	EMERGENCY VEHICLE PREEMPTION SYSTEM SPECIFICATIONS	700-15

708.1	System Description		700-15

708.2	Detailed Requirements		700-16

709	TRAFFIC SIGNALIZATION CONDUIT		700-17

709.1	General			700-17

709.2	Trenching and Backfilling For Conduit	700-18

709.3	Jacking Of Conduit		700-18

709.4	Materials			700-18

710	PREFORMED TAPE PAVEMENT MARKING		700-18

710.1	General			700-18

710.2	Conformability		700-18

710.3	Shelf Life		700-19

710.4	Color			700-19

710.5	Retro-Reflectivity		700-19

710.6	Durability and Replacement Provisions	700-20

710.7	Measurement Procedure For Determining Retained

Retroreflectance		700-20

SECTION 700 - TRAFFIC SIGNAL TECHNICAL SPECIFICATIONS

701	GENERAL

This specification describes the minimum design and operating requirements for traffic signal

controller assemblies. The City of Scottsbluff is developing an integrated traffic signal system

that will utilize the features described below. Initially, the system will be coordinating using

"time-base" techniques. Eventually the system will be interconnected with fiberoptic cables and

be supervised by a traffic responsive, closed loop master controller. Accordingly, all

controllers shall be equipped with necessary modules and software for full closed loop operation

utilizing fiberoptic interconnection. The use of external fiberoptic modems will not be allowed.

The controller, conflict monitor, detector amplifiers, cabinet, and auxiliary equipment shall be

as described below and shown in the plans accompanying this request. A closed loop master

controller will be purchased at a later date.

702	TRAFFIC SIGNAL CONTROLLER ASSEMBLY

702.1	General Design Requirements

(a)	The controller unit shall, as a minimum, meet the requirements of NEMA Standard TSI-

1989 parts 13 and 14. The controller unit shall contain, as a minimum, vehicle,

pedestrian and volume density timing on all phases. The controller unit shall also

contain time based coordination as a standard feature. These functions shall be

accomplished through the use of a 16 bit microprocessor to implement the timing

control logic.

(b)	Chassis - The controller unit shall consist of a chassis suitable for shelf

mounting, including processor module, power supply module, input/output module,

display module, keyboard module, and auxiliary input/output module. Space shall be

provided for a communications module for use in a closed loop environment.

(c)	Operator programming and data retrieval shall be by means of a menu driven display

and a keyboard located on the front panel of the unit.

(1)	The display shall be a liquid crystal display (LCD) and contain a minimum of 4

lines with 40 characters per line. The display shall have a 16 range adjustment

of contrast control and backlighted which automatically turns off 10 minutes

after the last key is pressed. The keyboard shall be a domed, tactile feedback,

membrane style keyboard. The display and keyboard shall be functional over the

NEMA temperature range of -34 F to +165 F.

(2)	The keyboard shall include keys which facilitate operation of a menu driven

program. It shall include dedicated cursor arrow keys, page up, page down, main

menu, prior menu, display contrast, run status, backlight control, clear,

enter, help, as well as the digits 0-9 and a decimal point. Generic hexadecimal

keypads will not be accepted. Context sensitive help screens shall be provided

giving a description of the functions on each screen.

(d)	Program data shall be retained in EEPROM, and mounted on a removable program card.

This card shall be suitable for transporting all programming data from one unit to

another, including the current real time and date. The program card shall not exceed

nine square inches and shall include a battery to maintain current time and date

while power is removed.

(e)	Non-program data such as volume log or MOE data may be stored in either battery

backed RAM or EEPROM. Whichever method is chosen, a minimum of 128K of such memory

shall be provided.

(f)	An RS232C connector shall be provided on the front panel to allow for controller to

controller transfer of data, printing of data and for uploading and downloading data

to a computer either directly or via dial-up telephone modem.

(g)	An auxiliary module shall be included to accommodate direct 115 VAC interconnect

based coordination, preemption inputs and outputs, and applications requiring

additional inputs and outputs. A CPC connector (MSD) shall be provided to

interconnect all inputs and outputs associated with the aforementioned functions.

(h)	An auxiliary module shall be included that provides necessary inputs and outputs for

closed loop system operation.

(1)	Modem - Communications with the system master requires a built in modem and

connectors for fiber-optic type cable.

(2)	Auxiliary Input - A separate connector for additional inputs for detectors and

conflict monitor status bits that report back to a central control system.

(3)	RS232C - A connector identical to Section F above allowing an event logging

conflict monitor to report directly to a remote location.

(i)	The chassis shall be constructed so that adequate ventilation is achieved without

any open holes in the top of the chassis. The chassis and circuit boards shall be

designed to allow for normal handling of such components without sustaining damage

due to electro-static discharges. Any disclaimers in the technical manuals or

printed on the chassis or any circuit boards suggesting that special handling is

required or suggesting that the warranty may be voided if subjected to such electro-

static discharges will be considered as evidence of defective design and will be

considered as grounds for rejection of the controller.

702.2	Functional Operation

In addition to those timing intervals and functions defined in NEMA TSI-1989 the

following features shall be provided:

(a)	A dimming input to the controller shall be provided that, when active, shall cause

designated circuits to be pulsed on and off in conjunction with the AC power

source. The result of the corresponding load switch output will be such that the

effective voltage to the signal bulbs will be approximately 70% of the line voltage.

The selection and mode of pulsing (positive or negative half wave) for each circuit

shall be programmed to balance the electrical loads in keeping with good engineering

practice.

(b)	Automatic Min Gap Recall shall be operator selectable. It shall be possible to not

automatically place a call on a phase if the phase reaches its minimum gap. If

enabled, the call would be placed after gap out termination of the phase.

(c)	Soft recall shall provide a recall for the phase(s) programmed, providing no other

serviceable calls are present.

(d)	Simultaneous Gap Out shall be operator selectable. If Simultaneous Gap Out is

enabled (standard NEMA), a phase will restart its passage timer upon demand

regardless of any previous green rest condition. If Simultaneous Gap Out is

inhibited, a phase will not restart its passage timer once it has rested waiting to

cross the carrier under dual ring operation.

(e)	Conditional service selectable for both vehicle and pedestrian calls. In dual ring

operation, vehicle conditional service allows an odd numbered phase to be serviced

out of sequence subject to other critical timing parameters. Pedestrian conditional

service allows pedestrian service if the pushbutton call arrives after the beginning

of green for the phase.

(f)	The overlap phases of an overlap shall be programmable through the keyboard. It

shall be possible to modify the normal operation of the overlap to inhibit green or

yellow indications during special phase colors, such as for right turn overlaps

when on during the through green. It shall also be possible to lag the clearance of

overlaps A-D from their parent phase by a programmable amount, using their own

yellow and red timing. The load switch drivers of any unused phase shall be

programmable as overlap outputs.

(g)	MUTCD Flash. The phases which will be serviced prior to entering MUTCD (planned)

flash and the phases serviced immediately following MUTCD flash shall be

programmable.

(h)	Dynamic control of maximum green time shall be provided on a cycle by cycle basis.

If a phase reaches the programmed maximum two consecutive cycles, the maximum time

is extended by a programmable increment up to a settable upper limit. If the phase

then gaps out two consecutive cycles, the maximum time is decreased by the increment

amount down to the programmed maximum time.

(i)	The ability to charge minimum green, passage time, walk, pedestrian clearance,

maximum green, recall and phase status shall be provided. Up to eight separate

schedules shall be programmable and selected by time of day or coordination program.

(j)	The unit shall provide a minimum of 24 vehicle detectors consisting of the 8

standard NEMA detectors, 8 on MSD and 8 on the communications module. Each detector

shall provide programmable phase assignment, detector switching capability, plus

stretch and delay timing operation.

(1)	Detector diagnostics - The unit shall provide the capability of optionally

monitoring each detector for acceptable operation based on its operation over

a programmable sampling period and range. A detector not meeting acceptance

criteria shall be considered failed. A failed detector can return to normal

status at the end of the next sampling period if it returns to within range

during that period.

702.3	Displays and Keyboard

(a)	Menu Format. The display shall operate in a true menu format whereby the display

lists, in English, various categories from which the user may select. The base

menu shall list the most general category choices such as program mode and real

time status. From this base menu, when a category is selected, a submenu appears

listing further choices such as security code, controller, coordination, time

clock, pre-emption, etc. Each submenu further breaks down the choices into more

specific categories until the specific sections of data can be obtained. The

display shall operate such that a user familiar with traffic terminology, but

unfamiliar with the display can successfully operate the display by following

menu selections.

(b)	Menu Modes. The base menu shall contain, as a minimum, a mode to observe the

controller timing and input/output status; a mode to read or program all settings;

and a utilities mode for data management.

(1)	The utilities menu shall allow the operator to perform as a minimum, the

following functions:

(a)  Loading backup timing for the controller, coordination, or time clock

data.

(b)  Clearing data to default settings for controller, coordination or time

clock data.

(c)  Transfer data to another unit, personal computer, or printer.

702.4	Time Clock

(a)	General. The internal time clock shall be a yearly programmable device consisting

of programmed event which are assigned to day programs (24 hours), such day programs

being assigned to week programs (7 days), such week programs being assigned to a

year program. The real time clock shall operate on a 99 year calendar.

(b)	Functional

(1)	Time clock coordination control. When enabled to do so, the time clock shall

be able to control the coordination command set, thereby selecting the cycle,

split, offset and system/free status in effect based on day program event

selections.

(2)	Time clock internal function control. When enabled, it shall be possible to

control functions by internal time clock without external wiring. As a minimum,

it shall be possible to control the following functions by time of day:

(a)  Coordination Cycle/Split/Offset

(b)  MUTCD Flash

(c)  Max II select

(d)  Inhibit Max, per ring

(e)  CNA I/II

(f)  Min Recall, all phases

(g)  Vehicle and Ped calls, per phase 1-8

(h)  Vehicle and Ped omits, per phase 1-8

(i)  Call Red Rest mode, per ring

(j)  Omit all Red Clearance, per ring

(k)  Enable Ped Recycle, per ring

(l)  Detector monitor low threshold inhibit

(m)  Detector monitor constant call inhibit

(n)  Enable dual entry

(o)  Conditional service enable

(p)  Simultaneous gap out inhibit

(q)  Disable interconnect (enable time base coord)

(r)  Inhibit volume density operation per phase

(s)  Lag phases 1, 3, 5, 7

(t)  Inhibit overlaps A, B, C, D

(u)  Inhibit Detectors, 1-16

(v)  Select Service Plan, 1-8

(w)  Select Max Plan, 1-8

(x)  Dimming

(3)	Sync reference modes. The coordination cycle in effect, when selected by time

clock, shall be referenced to the time clock by means of a time base reference

and not an input. The unit will automatically correct the cycle counter upon

power-up as well as on command to the time base reference. To provide

flexibility in adapting the unit to synchronize to other types of units, at

least four keyboard selectable methods consistent with industry standards of

sync referencing shall be provided.

(4)	Absolute zero reference. This is a non-once-per-day reference method in which

each cycle shall be individually referenced to a single point in time by a

keyboard initiated reset command. The unit will continuously update its

reference from this point on a cycle by cycle basis. The unit shall be capable

of automatically referencing back a minimum of 100 hours after power outage

without manual reset.

(5)	Time Clock outputs. The unit shall contain at least 13 circuits with outputs

on MSD. A minimum of these shall be general purpose outputs with the remainder

assigned to coordination functions.

(6)	Clock Set. It shall be possible to manually set the time clock for the correct

time to the correct hour, minute, second, year and date. Each output function

shall be capable of being programmed in increments of one second.

(7)	Selection Modes. The unit shall provide a method of choosing the source for

selection of the cycle, split, offset, flash and system commands. The sources

provided shall be manually through the keyboard, time clock, AC interconnect,

communications with time clock backup (closed loop system), or AC interconnect

with time clock backup.

702.5	Coordination

(a)	Coordination Features. The controller unit shall be capable of the following

coordination features:

(1)	Eight cycles

(2)	Four splits per cycle

(3)	Five offsets per cycle

(4)	Eight permissive periods per split

(5)	Eight force-offs per split

(6)	One pedestrian permissive, or automatic permissive

(7)	One dwell period per cycle

(b)	When using a hardwire interconnect system, any controller unit shall be able to

operate as a Master controller or as a secondary without requiring any changes in

the unit itself.

(c)	Time Base Coordination. The controller unit shall be capable of coordinated

operation in response to internally generated time clock commands selecting cycle,

split, and offset. In this mode the unit shall coordinate with other time base units

in the City of Scottsbluff without need of interconnect. The time clock shall

conform to requirements stated above.

(d)	Offset shall be selected by 115VAC input, FSK input from closed loop system, or by

the internal time clock. Offset transfer shall use either shortway, dwell, or

offset interrupter modes.

(e)	Force-off function shall cause the controller to terminate right-of-way on the

programmed phases. Force-offs shall be maintained until the green terminates.

(f)	Permissive periods shall allow flexibility in determining the beginning of each

non-coordinated phase by releasing HOLD and applying phase omits as programmed.

(g)	Adaptive split control shall allow split selection independent of commands from the

master or time clock. The split timing can be altered due to successive cycles with

phase/s terminated by force-off or by consistent activity of a queue detector on

that phase.

702.6	Preemption

(a)	The controller shall provide preemption capable of generating up to six distinct

sequences including low priority sequences. These sequences shall be either "hold

only" or a "sequence" preemptor that modifies the normal signal operation to suit

special situations required by emergency vehicles, trains, transit busses, etc.

(b)	Each sequence may be assigned a priority that allows higher priorities to override

and prevail over lower priority. Those of the same priority will be answered on a

first come, first serve basis.

(c)	Six preempt outputs shall be provided which will be active when called for by the

preempt sequence.

702.7.	Miscellaneous Features

(a)	Reports. It shall be possible for either the controller or conflict monitor to

record significant events and to generate a report from data logged by the

controller or conflict monitor. These reports can be transmitted to an external

printer or portable computer using the RS232 port on the front of either unit.

Data records shall be time and date stamped and shall include as a minimum, the

following types of records:

(1)	Power on/off, interruption

(2)	Power on self test diagnostics pass/fail

(3)	Conflict Monitor Status (Conflict, Red Fail, etc.)

(4)	On/off status and 8 user defined inputs

(5)	Remote Flash on/off

(6)	Manual Control enable on/off

(7)	Start and end of each pre-empt sequence

(8)	Cycle failure

(9)	Enter/exit system operation

(10)	Flasher failure (2 AC inputs)

(11)	Detector 1-24 out of threshold (Det 17-24=sys)

(12)	Detector 1-24 no activity (Det 17-24=system)

(13)	Detector 1-24 constant call (Det 17-24=system)

(14)	Detector 1-24 Return to normal (Det 17-24=system)

(15)	Phase 1-8 in/out of Detector Max Fail Recall mode

(b)	Measures of effectiveness (MOE) shall be recorded and stored in the controller.

These shall include but not be limited to volume per phase, green utilization,

phase termination, average speed over each detector loop, true speed between

specified detector loops.

702.8	Conflict Monitor

(a)	The conflict monitor shall comply in all aspects to the NEMA Standard TSI, 1989,

Part 6 with 12 input channels. It shall continuously monitor all green, yellow, red,

and walk circuits as well as the voltages within the controller and monitor. Liquid

Crystal Display (LCD) indicators shall be on the front of the monitor to indicate

the active channels, controller output, and the type of failure, if one should

occur. The LCD display shall be visible and operable over the entire temperature

range without the use of heaters or other external devices. The monitor circuitry

shall use microprocessor type logic. The monitor shall be compatible with the

controller and shall be designed and manufactured by the same factory as the

controller.

(b)	In the event of a power failure after a conflict has occurred, the monitor shall

retain in its memory the status of the display. It shall then display the same

indications upon restoration of power.

(c)	Three outputs shall be provided to be used as monitor status outputs. These shall

be available to allow status reporting to a remote location.

(d)	The monitor reset switch shall respond only to momentary operations. If the monitor

is in a fault mode, continuous operation of this switch shall not cause the monitor

to restore to normal signal operation.

(e)	The conflict monitor shall be capable of logging by time and date of occurrence all

types of failures, power on/off, and changes in front panel switch settings. As a

minimum, it shall store at least 140 events at any time. These events along with

current status of front panel switch settings, compatibility card programming and

intersection identification shall be capable of being printed on demand, either

directly from the unit or via a telephone hookup through the host controller to a

remote computer.

(f)	In addition to the basic monitor functions as prescribed by the NEMA Standard, the

following features shall be provided to enhance the safety of the intersection

operation. Each function shall be selectable by a switch on the front panel of the

unit.

(1)	Monitor minimum clearance time. This feature will place the intersection in

flash mode if the clearance intervals are less than a preset minimum time.

(2)	Watch dog monitor. This feature places the intersection in flash if the

controller "hangs-up" due to a failure of the controller microprocessor.

(3)	Individual channel monitoring. If certain combinations of simultaneous

indications (yellow and red, green and yellow, etc.) occur, the monitor shall

register a failure. This feature not only prohibits undesirable multiple

indications of the same channel but also anticipates conflicting displays

before they can occur.

(4)	Fault Re-Initialization. This function shall re-initialize the controller

upon exit from a failure mode either self-correcting or by pressing the

reset button.

(5)	CVM and 24 Volt Latch. This feature will require the reset button to be

pressed in order to clear these failures.

702.9	Loop Detector Amplified

Loop detector amplifiers shall conform to the following requirements.

(a)	Low power C-MOS digital microprocessor design with relay output.

(b)	Completely self tuning--instant upon application of power.

(c)	Loop inductance range--20 to 2500 microhenries.

(d)	Loop frequency--20 to 50 kilohertz with three switch selectable frequencies.

(e)	Sensitivity--0.0025% to 1.35 inductance shift with ten thumbwheel switch selectable

ranges.

(f)	Pulse mode--100 to 150 msec per vehicle. If a vehicle stalls on the loop, remainder

of loop area will detect vehicles two seconds after stall condition. After stalled

vehicle leaves the loop area detector recovers full sensitivity in less than 750

msec.

(g)	Presence mode--minimum of 4 minutes for any vehicle detected.

(h)	Lightning protection--built in protection to withstand a 10 microfarad capacitor

charged to 2000 volts between loop terminals and chassis ground, withstand a 10

microfarad capacitor charged to 1000 volts across open loop terminals.

(i)	Grounded loop--loop isolation transformer to allow operation with a single point

short between loop and ground.

(j)	Reliable operation of amplifier up to one mile from loop.

(k)	If required on Plans, the following timing functions shall be provided:

Delay time--up to 60 seconds in 1 second steps.

Extension time--up to 15 seconds in 0.25 second steps.

Delay override--120VAC applied to pin J.

Both delay and extension timed with digital timer and fully operable at all times

and can be used together.

(l)	All switches and controls on front panel. LED indicator light on front of chassis.

(m)	"Smart" indicator operation to differentiate between normal call status, delay

timing, extension timing, and failed or out of range loop condition.

(n)	If required on Plans, a second output shall be included for obtaining count data

from large area detection loops or for a separate system detector output to master

controller.

702.10	Cabinet

The controller cabinet shall be made of sheet aluminum alloy. The cabinet style and size

shall be a Type P: 55"Hx44"Wx26"D for signal sequence over four phases. The controller

cabinet shall be mounted on a 5' x 8' x 4" P.C. concrete pad.

The following features and accessory equipment shall be included:

(a)	Unpainted natural aluminum finish.

(b)	Gasketed main door with standard lock and 2 keys and doorstop.

(c)	Gasketed police panel door with police lock, 2 keys, flash switch and signal

shutdown switch.

(d)	Thermostatically controlled fan installed in plenum in roof of cabinet. Turn-on

temperature adjustable between 70 and 160 degrees F.

(e)	Filtered air intake near the bottom of the cabinet, designed to prevent the entrance

of dust, insects and blowing rain and snow. Filter removable for cleaning or

replacement.

(f)	Duplex receptacle with ground fault interrupter, lamp base with toggle switch.

Outlet and lamp to be fused ahead of the main circuit breaker.

(g)	Main circuit breaker, line filter, lightning arrestor.

(h)	Solid state flasher conforming to NEMA Standard TSI Part 8, Type 3. Heavy duty flash

transfer relays shall be provided.

(i)	Solid state load switches conforming to NEMA Standard TSI Part 5 shall be provided

in sufficient numbers to provide the sequence shown in the plans. The cabinet

backpanel shall provide for 12 fully wired receptacles for these load switches.

Receptacles shall be hard-wired.

(j)	Fused input for interconnect cable complete with MOV surge protection.

(k)	Maintenance switches inside the cabinet shall include the following:

(1)	Stop Time Control

(2)	Timer Power

(3)	Flash

(4)	Vehicle detector input for each phase in use.

(5)	Pedestrian input for each phase in use.

(l)	Detector harnesses as necessary.

(m)	Relay and photocell to implement night-time dimming.

703	TRAFFIC SIGNALIZATION SYSTEM

703.1	General

All traffic signal supports, traffic and pedestrian signal lights, traffic and pedestrian

actuation equipment shall meet current State of Nebraska Department of Roads

specification except as outlined in these plans and specifications.

703.2	Pole Design

The pole shall be designed to support the signal load shown in the plans plus one

additional signal head per span and shall withstand wind velocities up to 100 mph.

The design weight of the signal head shall be 75 pounds with a surface area of 12.5

square feet.

703.3	Mast Arm Design

The poles shall be designed to support the required signal and luminaire load, mast arms

with 10 lbs. of ice per linear foot, signal and lighting cables and shall withstand

winds with velocities up to 100 mph.

The manufacturer shall state the necessary amount of pole rake necessary for the pole

to set plumb under the required signal and lighting load in the plans.

703.4	General Signalization

(a)	Traffic signal mast arms, luminaire mast arms, luminaire extensions and pole shafts

shall be supplied with 1" I.D. rubber grommets for cable inlets. Signal mast arms

shall also be supplied with 1" rubber grommets for the number of signals specified.

All inlet holes shall be drilled in the field by the contractor.

(b)	Pole caps shall be provided with each pole shaft or luminaire extension, and signal

mast arm.

(c)	All hand holes shall have a minimum opening of 4" x 6". Pole shafts and luminaire

extensions shall be supplied with hand hole covers. The hand hole shall be

reinforced to maintain full strength of the pole.

(d)	Signal mast arms shall have a maximum rise of 5 degrees unloaded and a minimum rise

of 0 degrees at the end of the mast arm when fully loaded.

(e)	Each pole shaft, luminaire extension, luminaire arm and signal arm shall be

furnished with all miscellaneous hardware necessary to complete assembly.

(f)	The pole shaft, luminaire extension, luminaire arm and signal arm shall be

galvanized to comply with ASTM-A123.

(g)	All miscellaneous hardware shall be galvanized to comply with ASTM-A153. (Except

threaded fasteners under 3/8 inch diameter.)

(h)	A grounding nut and service post or ground lug for accommodation of a No. 6 AWG

Copper wire shall be provided on the inside of the pole shaft directly opposite the

hand hole opening. No grounding provisions will be allowed on the hand hole frame.

(i)	Traffic signal poles, mast arms, luminaire extensions, luminaire arms, luminaires,

all signalization and detection equipment, the luminaire and any other miscellaneous

hardware shall meet current State of Nebraska Standards.

(j)	All wiring contained within a signal pole-mast arm-luminaire, pull box, controller,

etc., shall be considered subsidiary to that item of work and will not be paid for

directly.

(k)	The location of all aerial and underground utility facilities may not be indicated

in these plans. Underground utilities whether shown or not will be located and

flagged by the utilities upon request of the contractor. No excavation will be

permitted in the area of underground utilities until all such facilities have been

located and identified tothe satisfaction of all parties. The contractor will be

responsible for protection of all underground and aerial utilities and

constructions.

(l)	All surface materials that are disturbed by excavation and backfilling operations

shall be replaced and restored in kind equal to or exceeding the original condition.

(m)	All material (EXCEPT where stated) shall be furnished and installed by the

contractor except for the controller which the City will furnish and the contractor

will install. The controller will be furnished to the contractor at the City Shop,

1103 3rd Avenue in the City of Scottsbluff, Nebraska. The contractor shall be

responsible for transportation of the controllers to the work sites. The cabinet

shall be supplied along with the controller, by the City.

(n)	The traffic signals shall be of the configuration shown and shall include one piece

black backplates. The signals shall be mounted as shown. All mountings shall be such

that the actual location of the signal mast arm or luminaire can be adjusted in the

field.

(o)	Wiring shall be done in accordance with State and local codes to produce the desired

phasing.

(p)	The construction of this project shall be scheduled and done in such a manner that

the existing traffic control system can be kept in service until the new signals are

ready for use. If during the course of construction it becomes necessary to remove

the existing traffic control device the contractor shall be held wholly responsible

for the costs of any temporary traffic control device the Engineer may require.

(q)	All wiring shall be placed underground in PVC conduit. Where jetting, pushing or

augering is required, RGS conduit may be used. Open cuts will only be allowed

through pavement which is being removed and replaced as part of this project.

(r)	The power supply to the existing traffic signal system shall be adapted by the

contractor for use with the new traffic signals.

704	TRAFFIC POLE FOUNDATION SPECIFICATIONS

704.1	General

The pole foundation shall be round. The excavation shall be to the neat lines of the

foundation, only the top two feet may be formed.

704.2	Reinforcing Steel

#5 rebar - 5/8" x 7'4", 8 per foundation

#5 rebar - 5/8" bar bent as shown, 8 per foundation

704.3	Ground Rod (5/8" x 17')

The ground rod should be placed before the concrete is poured and located as shown in

foundation detail. It shall extend at least eight inches above top of finished foundation

and shall extend a minimum of eight feet into the ground below the foundation.

704.4	Anchor Bolts

Anchor bolts shall be 1-1/2" diameter, 54" long with a 6" hook and shall be threaded.

Each anchor bolt shall be supplied with two hexagonal nuts and two flat washers. Anchor

bolts shall be 50,000 psi minimum yield strength.

704.5	Conduit Bends

Conduit bends shall be 90 degrees. They shall be located a minimum of 30 inches below

ground level. Standpipe conduit 4 inch minimum above top of finished foundation.

704.6	Spare Bend

There shall be a minimum of one spare conduit bend installed in each foundation with

both ends plugged and free of debris and moisture.

704.7	Concrete

Concrete shall be Class 47B.

705	TRAFFIC DETECTION LOOPS

Traffic detection loops shall be saw cut in existing pavement

The location of traffic detection loops shall NOT coincide with any existing alley, drive or

other location where traffic may trigger the loop but not enter the intersection. All front

loops shall be placed adjacent the PC unless stated otherwise. All loop locations shall be

approved by the Engineer prior to placement of the loop.

Loops located in areas where new pavement is installed shall be placed 2" below the paving

section in a 4" sand base course.

Loops located in areas to be overlaid or where no surfacing will be placed shall be sawn into

the existing paving section. The loops shall be sawn into the existing pavement by the

contractor. All sawn cuts will penetrate into concrete where possible. In general, the loop

cuts shall be 3 inches in depth at locations where no overlay will occur and 2 inches at

locations that have been milled prior to an overlay. The width of the cut shall be no less than

3/8 inch.

Saw cuts shall be completely filled with any of the sealants accepted by the Nebraska Department

of Roads for this purpose, or an equivalent approved by the Engineer. Backer Rod will be used to

prevent sealant from bonding to the loop wire.

The loop wire shall be DSI-116 loop wire manufactured by Detector Systems, Inc. or an approved

equal.

The feeder wire shall be DSI-1602 feeder cable manufactured by Detector Systems, Inc. or an

approved equal.

Each traffic detention loop shall have its own feeder cable unless otherwise noted.

706	STREET NAME SIGN

706.1	General

The street name sign shall be two faced, internally illuminated, with photocell.

The sign shall be an FL-SNS-6-800-2-2W, as manufactured by National Sign and Signal

Company, or an approved equal.

The sign and installation shall comply with all City of Scottsbluff codes.

707	EMERGENCY VEHICLE PREEMPTION SYSTEM

707.1	System Description

This specification describes the minimum operating requirements of a siren activated

Emergency Vehicle Preemption system (EVP). The vehicle siren, which is standard equipment

on all emergency vehicles, registers its presence by activating the siren's "yelp" mode.

This system provides a method that allows an emergency vehicle to have priority over

other vehicles and pedestrians at a traffic signal. All approaches to a signal serving

vehicular traffic shall be equipped to provide priority to emergency vehicles. Under no

circumstances shall any vehicular approach to a signal be unprotected. The system

components are as follows:

(a)	detectors (directional microphones) at each signal that detect the imminent arrival

of an emergency vehicle...

(b)	a phase selector located in the signal controller cabinet that processes the input

detector information and produces an appropriate output to the signal controller.

The signal controller will be programmed for the special preemption sequence and timing

necessary for each individual signal. Modern controllers allow considerable flexibility

in developing this sequence and timing but the most common practice is to provide a

"green" priority signal to the emergency vehicle and a "red" signal to all other traffic.

If shown on the plans, a confirmation light shall be installed on each approach that

informs the driver whether the signal actually is under preemption control rather than

normal operation.

The system shall be fully compatible with the EVP system currently used by the City of

Scottsbluff. The system shall be manufactured by Emergency Preemptions Systems, Inc. or

as approved by the Engineer.

707.2	Detailed Requirements

(a)	Detector Devices

The detectors shall be specially designed microphone that are positioned on the

traffic signal poles in such a manner that each approach to the signal is adequately

detected. The detectors shall not be affected by fog, rain, ice, snow or other

adverse weather. They shall be directional with an 18 degree cone of sensitivity.

They shall be weatherproof and designed to withstand electrical transients normally

encountered in the ambient outdoor environment. Electrical cable from the detector

to controller cabinet shall be 18 AWG 2-conductor, twisted, shielded pair such as

Belden 8762 or equal. In some cases, a multiple pair cable can be used if several

microphones are located on the same pole.

Detectors shall be located in the plans and shall be installed in strict accordance

with the manufacturers recommendations.

(b)	Phase Selector Device

The electronic device located in each signal controller cabinet is commonly referred

to as a phase selector. This device is used to decode the information from each

detector and produce suitable outputs to the controller. It shall be designed to

meet the environmental and electrical standards specified by NEMA Standard TS-1. It

shall be designed using microprocessor circuitry.

Adjustment and calibration of the EVP system shall be a function of detector

placement and phase selector inputs. The phase selector adjustments shall have

resident software that allows range and sensitivity adjustment to be made using a

portable computer. Unless specified in the contract documents, the portable computer

shall not be furnished as part of this project.

The phase selector shall have adequate memory to record all system activity. Each

access to the system shall be recorded with the date, time, duration of access,

quality of the emitter/detector input signal, along with any other pertinent

information. There shall be sufficient memory to store up to 4000 usage events. The

event log shall be accessible by either a direct connection to the unit or remotely

by a dial-up telephone modem attached to the unit.

(c)	Technical Support Services

The manufacturer and/or supplier shall provide training to the agency responsible

for the operation of the signal system. This shall include operational, maintenance,

and trouble-shooting procedures.

Training shall also be provided for all drivers of emergency vehicles that are

likely to utilize the EVP system. It shall be the manufacturers responsibility to

locate all such drivers and provide on-site training consistent with the drivers

employment schedules.

708	EMERGENCY VEHICLE PREEMPTION SYSTEM SPECIFICATIONS

708.1	System Description

This specification describes the minimum operating requirements of a siren activated

Emergency Vehicle Preemption system (EVP). The vehicle siren, which is standard equipment

on all emergency vehicles, registers its presence by activating the siren's "yelp" mode.

This system provides a method that allows an emergency vehicle to have priority over

other vehicles and pedestrians at a traffic signal. All approaches to a signal serving

vehicular traffic shall be equipped to provide priority to emergency vehicles. Under no

circumstances shall any vehicular approach to a signal be unprotected. The system

components are a follows:

(a)	detectors (directional microphones) at each signal that detect the imminent arrival

of an emergency vehicle.

(b)	a phase selector located in the signal controller cabinet that processes the input

detector information and produces an appropriate output to the signal controller.

The signal controller will be programmed for the special preemption sequence and timing

necessary for each individual signal. Modern controllers allow considerable flexibility

in developing this sequence and timing but the most common practice is to provide a

"green" priority signal to the emergency vehicle and a "red" signal to all other traffic.

If shown on the plans, a confirmation light shall be installed on each approach that

informs the driver whether the signal actually is under preemption control rather than

normal operation.

The system shall be fully compatible with the EVP system currently used by the City of

Scottsbluff. The system shall be as manufactured by Emergency Preemption Systems, Inc. or

as approved by the Engineer.

708.2	Detailed Requirements

(a)	Detector Devices

The detectors shall be specially designed microphones that are positioned on the

traffic signal poles in such a manner that each approach to the signal is adequately

detected. The detectors shall not be affected by fog, rain, ice, snow or other

adverse weather. They shall be directional with an 18 degree cone of sensitivity.

They shall be weatherproof and designed to withstand electrical transients normally

encountered in the ambient outdoor environment. Electrical cable from the detector

to controller cabinet shall be 18 AWG (minimum) 2-conductor, twisted, shielded pair

such as Detector Systems DSI-1602, Belden 8762, or equal. In some cases, a multiple

pair cable can be used if several microphones are located on the same pole.

Detectors shall be located as shown in the plans and shall be installed in strict

accordance with the manufacturers recommendations.

(b)	Phase Selector Device

The electronic device located in each signal controller cabinet is commonly referred

to as a phase selector. This device is used to decode the information from each

detector and produce suitable outputs to the controller. It shall be designed to

meet the environmental and electrical standards specified by NEMA Standard TS-1. It

shall be designed using microprocessor circuitry.

Adjustment and calibration of the EVP system shall be a function of detector

placement and phase selector inputs. The phase selector shall have resident software

that allows range and sensitivity adjustment to be made using a portable computer.

Unless specified in the contract documents, the portable computer shall not be

furnished as part of this project.

The phase selector shall have adequate memory to record all system activity. Each

access to the system shall be recorded with the date, time, duration of access,

quality of the emitter/detector input signal, along with any other pertinent

information. There shall be sufficient memory to store up to 4000 usage events. The

event log shall be accessible by either a direct connection to the unit or remotely

by a dial-up telephone modem attached to the unit.

(c)	Technical Support Services

The manufacturer and/or supplier shall provide training to the agency responsible

for the operation of the signal system. This shall include operational, maintenance,

and trouble-shooting procedures.

Training shall also be provided for all drivers of emergency vehicles that are

likely to utilize the EVP system. It shall be the manufacturers responsibility to

locate all such drivers and provide on-site training consistent with the drivers

employment schedules.

709	TRAFFIC SIGNALIZATION CONDUIT

709.1	General

(a)	Conduit shall be of the size designated in the plans. Where jacking or augering of

conduit is required, GRS will be used. Everywhere else, conduit shall be PVC.

Conduit systems shall be constructed in accordance with NEC.

(b)	Conduit sizes required are shown in the plans and shall be interpreted to mean the

minimum "trade size" permitted for the application; the contractor may, at his

option and expense, substitute a larger size.

(c)	Drainage shall be provided for each conduit run by holes drilled in the conduit at

the low point. The holes shall be deburred.

(d)	Fittings used with galvanized rigid steel conduit shall be galvanized steel or

galvanized malleable iron; fittings of aluminum or zinc alloys are not acceptable.

Fittings and cement used with plastic conduit must be compatible with the conduit

material.

(e)	Field bends must be properly formed with appropriate tools, and must not result in

reduced cross sectional area of the conduit.

(f)	Exposed field cut threads on metallic conduit, and any area where galvanizing has

been removed, shall be painted with one coat of an approved zinc rich paint.

(g)	All conduit terminations shall have bells or bushings.

(h)	Spare conduits shall be capped or plugged with standard fittings.

(i)	Unless otherwise provided, or directed by the Engineer, underground conduit shall be

placed at least 30 inches below finished grade.

(j)	The locations of conduit runs, as indicated in the plans, may be altered at the

direction of the Engineer to accommodate field conditions. Conduit should be routed

to minimize damage to existing trees and shrubs.

709.2	Trenching and Backfilling For Conduit

(a)	Trench width shall be the minimum practical dimension needed to place the conduit.

(b)	At least 1 cubic foot of gravel shall be placed beneath the drainage holes in the

conduit.

(c)	Backfill material shall be free of unsuitable materials and compacted in a manner

acceptable to the Engineer.

709.3	Jacking Of Conduit

Conduit placed under surfaces which are not to be disturbed may be jacked or augered.

Jacking pits shall, when feasible, be at least two feet beyond any type of pavement.

Excessive use of water will not be permitted. Non-metallic conduits may be placed in an

over-size metal conduit sleeve which has been jacked or augered in place at no

adjustment in compensation.

709.4	Materials

(a)	Galvanized rigid steel conduit (GRS) shall meet the requirements of the NEC Article

346 and Underwriters Laboratories UL-6.

(b)	Polyvinylchloride conduit (PVC) shall be rigid PVC conduit, schedule 40; it shall

meet the requirements of the NEC Article 347, NEMA Standard TC-2, and UL-651.

710	PREFORMED TAPE PAVEMENT MARKING

710.1	General

The pavement marking tape shall consist of white or yellow weather resistant, retro-

reflective film which shall provide a neat and durable marking that will not flow or

distort due to temperature variations; shall show no appreciable fading, lifting or

shrinkage throughout the life of the marking; and shall show no significant tearing,

rollback, movement or other signs of poor adhesion under normal traffic conditions as

long as the road surface remains stable.

710.2	Conformability

Tape shall be capable of being inlaid during the application of the final course of new

asphaltic surfaces and overlaid on existing Portland Cement concrete surfaces in

accordance with manufacturer's recommendations. Tape shall be capable of conforming to

pavement contours, breaks and faults through the action of traffic at normal temperatures

and shall be capable of being applied to previously applied material of the same

composition under normal conditions of use.

710.3	Shelf Life

The marking materials shall be manufactured and packed in such a manner as to permit

storage at normal shelf temperature for a period of not less than one year from the date

of purchase.

710.4	Color

Tape shall consist of high quality materials and pigments blended to provide consistent

day time and night time color conforming to standard colors throughout the useful life

of the marking.

The daytime color of the marking material shall conform to the following chromaticity

requirements:

Reflectance

Limit Y (%)

Color_____1_____________2_____________3_____________4________

__x__  __y__  __x__  __y__  __x__  __y__  __x__  __y__  min     max

White  0.290  0.315  0.310  0.295  0.330  0.360  0.350  0.340  65      -

Yellow 0.492  0.435  0.536  0.463  0.512  0.486  0.474  0.455  36      59

Measurements of color shall be made in accordance with ASTM E 1349, using illuminant C

and 0/45 (45/0) geometry. Calculations shall be in accordance with ASTM E 308 for the 2

degree (CIE 1939) observer.

710.5	Retro-Reflectivity

Tape shall provide initial and continuing retroreflectivity so that when measured in

accordance with ASTM D 4061 the following requirements shall be met. The photometric

quantity to be measured shall be specific luminance (SL) and shall be expressed as

millicandelas per square meter per lux [(mcd x m-2) x lux-1]. The English system

equivalent shall be millicandelas per square foot per footcandle. The test distance

shall be 15 meters (50 ft.) and the sample size shall be a .61m x .76m rectangle (2.0

ft. x 2.5 ft.).

Initial Retroreflectance

White           	            Yellow

Entrance Angle                 86.0 degrees  86.5 degrees    86.0 degrees  86.5 degrees

Observation Angle              0.2 degrees   1.0 degrees     0.2 degrees   1.0 degrees

Specific Luminance (SL)        1100          700             800           500

(mcd x m-2) x 1x-1

710.6	Durability and Replacement Provisions

The manufacturer shall provide replacement materials for tapes determined to be

inadequate traffic control devices or failing to meet minimum retained retroreflectance

requirements as described below for a period of six years following the date of

installation when installed as skip lines according to the manufacturer's

recommendations.

Minimum Retained Retroreflectance

White               Yellow

Entrance Angle                 86.5 degrees        86.5 degrees

Observation Angle              1.0 degrees         1.0 degrees

Specific Luminance (SL)        100                 100

(mcd x m-2) x 1x-1

710.7	Measurement Procedure For Determining Retained Retroreflectance

Measurement of retained retroreflectance for replacement purposes shall proceed as

follows:

(a)	A visual night time inspection shall be made with a manufacturer's representative

and a representative of the City present to identify areas of the installation which

appear to be below the specified minimum reflectance values.

Areas which appear to be below the minimum retained reflectance values shall be

identified as Zones of Measurement. To qualify for material replacement, a Zone must

be at least 360 feet (110 meters) in road length.

(b)	within each Zone, reflectance measurements shall be taken at specified checkpoints

as described below:

(1)	Zones measuring from 360 feet to 1080 feet (110 to 330 meters) in length:

Two measurements shall be taken on each skip (one measurement at each end of

the skip).

(2)	Zones measuring from 1081 feet to 6 miles (331 to 9600 meters) in length:

A total of 18 measurements shall be made in each of three checkpoints within

the zone including the start point, the midpoint, and the end point. Two

measurements shall be taken on each of nine skips (one measurement at each end

of the skip) within each checkpoint.

(3)	Zones greater than 6 miles (9600 meters) in length:

A total of 18 measurements shall be made in each checkpoint (one measurement at

each end of nine skips). Checkpoints will be located at the start point, end

point and at approximately 3 mile (4800 meter) intervals throughout the Zone.

(a)  Reflectance Measurement at the Checkpoints

All reflectance measurement shall be made on a clean, dry surface at a

minimum temperature of 40 degrees F (4 degrees C). The test instrument

shall be an "Ecolux" Brand Retroreflectometer. This instrument employs a

measurement geometry of 86.5 degrees entrance angle and 1.0 degrees

observation angle.

(b)  Evaluation of Reflectance Measurements

All reflectance measurements within the Zone shall be averaged to

determine if the minimum retained reflectance requirement has been met.

SECTION 800

LANDSCAPE IMPROVEMENTS

SECTION 800 - LANDSCAPE IMPROVEMENTS

TABLE OF CONTENTS		                     PAGE

801	GENERAL PROVISIONS 	                     800-1

801.1	Description	                     800-1

801.2	Quality Assurance	                     800-1

801.3	Preparation	                     800-1

802	SITE PREPARATION		                     800-1

802.1	General		                     800-1

802.2	Clearing and Grubbing	                     800-1

802.3	Vegetation Stripping	                     800-1

802.4	Soil Scarification and Rototilling	                     800-2

802.5	Removal of Miscellaneous Materials	                     800-2

802.6	Protection of Existing Trees and Shrubs                  800-2

803	GRADING	    		                     800-2

803.1	General		                     800-2

803.2	Testing		                     800-3

803.3	Materials		                     800-3

803.4	Process		                     800-3

803.5	Cleanup and Maintenance	                     800-4

803.6	Inspections	                     800-4

804	SOIL PREPARATION		                     800-4

804.1	General		                     800-4

804.2	Materials		                     800-4

804.3	Preparation	                     800-5

804.4	Inspections	                     800-6

805	SEEDING SPECIFICATIONS	                     800-6

805.1	General		                     800-6

805.2	Materials		                     800-6

805.3	Process		                     800-7

805.4	Cleanup and Maintenance	                     800-8

805.5	Inspections	                     800-8

805.6	Warranty		                     800-9

806	SODDING SPECIFICATIONS	                     800-9

806.1	General		                     800-9

806.2	Materials		                     800-9

806.3	Process		                     800-9

806.4	Cleanup and Maintenance	                     800-10

806.5	Inspections	                     800-10

806.6	Warranty		                     800-10

807	PLANTING SPECIFICATIONS	                     800-10

807.1	General		                     800-10

807.2	Materials		                     800-11

807.3	Process		                     800-12

807.4	Cleanup and Maintenance	                     800-15

807.5	Inspection	                     800-15

807.6	Warranty		                     800-15

808	TREE PRUNING SPECIFICATIONS	                     800-15

808.1	Safety Standards Tree Trimming and Tree Removal          800-15

809	IRRIGATION SYSTEMS	                     800-16

809.1	General	                     	                     800-17

809.2	Materials		                     800-17

809.3	Site Conditions/"As-Builts"	                     800-20

809.4	Excavation	                     800-20

809.5	Process		                     800-20

809.6	Inspections	                     800-22

809.7	Warranty		                     800-22

810	RECREATION FACILITIES	                     800-22

810.1	General		                     800-22

810.2	Playgrounds	                     800-23

810.3	Athletic Fields	                     800-23

810.4	Tennis Courts	                     800-23

810.5	Trails and Sidewalks	                     800-23

810.6	Recreation Facility Lighting	                     800-24

SECTION 800 - LANDSCAPE IMPROVEMENTS

801	GENERAL PROVISIONS

801.1	Description

These Standards and Specifications apply to all landscape projects which shall be

constructed in the City by private interests and accepted by the City for ownership or

maintenance. It is anticipated that additional, more detailed specifications shall be

prepared for each project, as needed.

801.2	Quality Assurance

Comply with all applicable local, state and federal requirements regarding materials,

methods of work and disposal of excess and waste materials.

Submit a traffic control plan, if required, for approval by the Traffic Engineer.

The City shall not be held liable for any consequences of a contractor's noncompliance

with these Standards and Specifications or any local, state, or federal regulations.

801.3	Preparation

Examine the areas and conditions under which site work is to be performed. Notify the

City regarding any unsatisfactory conditions.

Consult the records and drawings of adjacent work and of existing services and utilities

which may affect site work operations.

802	SITE PREPARATION

802.1	General

The Responsible Party shall provide all labor, materials, and equipment necessary to

complete site preparation work as shown on the drawings approved by the City Engineer

and as stipulated in these Standards and Specifications. All features to be retained

shall be properly protected in a manner approved by the City Engineer. The Responsible

Party shall identify and stake all surface and subsurface features of the project area,

including all property corners. Refer to subsections 103 and 503 of these Standards and

Specifications for related information.

802.2	Clearing and Grubbing

Refer to subsection 503.2 of these Standards and Specifications.

802.3	Vegetation Stripping

Existing vegetation designated for removal within the construction limits shall be

stripped to a depth of two inches below existing grade and disposed of by the

Responsible Party prior to beginning work. Topsoil shall be stripped to its full

depth, as approved by the City Engineer, and stockpiled on-site for later use. This

shall remain the property of the City of Scottsbluff.

802.4	Soil Scarification and Rototilling

All areas to be planted shall be scarified and rototilled to a six inch depth. (See

subsection 802.6 for protection of existing trees and shrubs.)

802.5	Removal of Miscellaneous Materials

Refer to subsection 503.3 of these Standards and Specifications.

802.6	Protection of Existing Trees and Shrubs

A tree and shrub protection plan must be submitted to the City Engineer for review and

approval prior to beginning work. The existing condition of all trees and shrubs in the

construction area shall be reviewed by the City Engineer. Any activity determined by the

City Engineer to be injurious to existing tress and shrubs shall not be permitted without

an acceptable, pre-approved impact mitigation plan in a form specified by the City

Engineer. These activities include grading, rototilling, equipment storage, vehicle

parking, stockpiling of soil, or other activities which cause soil compaction or

disruption. Trees or shrubs damaged during construction shall be valued in accordance

with the latest edition of Valuation of Landscape Trees, Shrubs, and Other Plants

(published by the International Society of Arboriculture). The Responsible Party shall

develop, and the City Engineer shall approve, a plan to add plant materials (equal in

dollar value to those damaged) to the site.

803	GRADING

803.1	General

The Responsible Party shall provide all labor, materials, and equipment necessary to

complete all grading work as shown on the approved drawings and as stipulated in these

Standards and Specifications. Refer to subsections 802 and 804 for related information.

The following general design standards shall apply:

(a)	Positive drainage, at a gradient suitable for the surface material, shall be

maintained into all proposed or existing drainageways. Ponding of water shall be

avoided, except in designated detention areas, in order to minimize compaction and

undermining problems.

(b)	Slopes shall not exceed four horizontal to one vertical for all areas to be planted

with grasses. Slopes should generally not exceed three horizontal to one vertical

for all other landscape areas; however, slopes up to two horizontal to one vertical

may be permitted for limited areas under extenuating circumstances, provided that

such slopes can be suitably stabilized.

(c)	Transitions from existing to proposed grades, and from gentle to steep grades

within the site, shall be rounded off to minimize sharp contrasts in landforms and

to prevent "scalping" by mowing equipment.

803.2	Testing

All classification testing shall be performed by a qualified independent testing

laboratory under the supervision of a registered professional engineer specializing

in soils engineering at the expense of the Responsible Party. The Responsible Party

shall coordinate with and fully comply with all recommendations made by the testing

agency.

803.3	Materials

All materials and methods of construction shall comply with pertinent standards of the

American Society for Testing Materials (ASTM) and the American Association of State

Highway and Transportation Officials (AASHTO).

On-site soils shall be used whenever feasible. When necessary to import soil materials,

such materials shall be subject to testing, and to City approval. When unacceptable

materials have been identified on-site, such materials shall be removed by the

Responsible Party and disposed of off-site.

803.4	Process

All applicable safety standards shall be followed for grading operations.

All grading operations shall be tested and inspected in accordance with these

Standards and Specifications.

The Responsible Party shall establish the horizontal and vertical limits of grading

through use of stakes, properly labeled, and shall have such staking approved by the

City Engineer.

No grading operations shall be permitted on a soft, spongy, frozen, unstable, or

otherwise unacceptable subgrade, as determined by the City Engineer.

All disturbed soils shall be periodically wetted to minimize blowing dust, as required

by the City Engineer. Refer to subsection 805.3(c) regarding stabilization of graded

areas.

When filling is required to meet the desired grade, each lift of the fill material

shall not exceed eight inches in loose depth. The Responsible Party shall thoroughly

mix fill materials to secure a suitable uniform moisture content and to insure

uniform density and proper compaction. Each layer shall be thoroughly compacted by

roller or vibratory equipment which is suitable for the type of embankment material,

to densities suitable for the final surface material (90 percent for planted areas and

95 percent for paved areas, in accordance with Standard Proctor Method). The City

shall reserve the right to have graded areas tested at appropriate times and locations,

at the Responsible Party's expense.

Final rough grade shall allow for specified soil amendments and subsurface materials

required for finished surfaces. The final rough grade shall be surveyed and staked

by the Responsible Party, and inspected by the City prior to soil preparation

operations.

803.5	Cleanup and Maintenance

All on-site and off-site areas disturbed as a result of grading operations shall be

renovated to original conditions or suitably cleaned up for subsequent construction

procedures. All excess materials shall be removed from the project area.

The Responsible Party shall protect all graded areas from unnecessary disturbance. The

Responsible Party shall repair all areas which may become eroded, settled or rutted

during the warranty period (one year following initial acceptance of the project) to

meet original specifications.

803.6	Inspections

Refer to subsection 106.3 of these Standards and Specifications.

The following inspections are required:

1.	Pre-construction.

2.	Following weed eradication.

3.	Following topsoil stripping and stockpiling.

4.	Following initial rough grading staking.

5.	During rough grading operations, at stages agreed upon by the Responsible Party

and the City Engineer prior to the start of grading operations, and as the City

Engineer may subsequently determine.

6.	At completion of rough grading.

Any work deemed by the City Engineer to be faulty or not in accordance with the

approved drawings and these Standards and Specifications shall be promptly corrected.

804	SOIL PREPARATION

804.1	General

The Responsible Party shall provide all labor, equipment, materials, and water

necessary to complete soil preparation for planting areas as required by the approved

drawings and these Standards and Specifications.

804.2	Materials

(a)	Organic Materials

Organic soil amendments shall be a well-rotted manure, peat, or approved equal (cow

manures should be used with caution, due to their high salt content); multiple

materials may be used. All organic materials shall have a pH of less than 7.5,

organic content of at least 40 percent, and salt content less than 12 mmhos/cm.

Organic material shall be free of unrotted sawdust, wood chips and chemical

contaminants. All sources shall be approved by the City Engineer prior to on-site

delivery; a lab analysis shall be provided for review by the City Engineer.

(b)	Fertilizer

Prior to any application of fertilizer, a soil analysis shall be performed at the

Responsible Party's expense by a qualified agricultural testing lab approved by

the City Engineer. Samples for testing shall be acquired using a coring tool to

take representative samples to a depth of at least eight inches. The fertilizer

applied shall be in the formulation and at the rate recommended in the soil

analysis for the intended crop.

(c)	Water Retention Amendments

Soil amendments designed to enhance water availability for plant materials may be

used when approved by the City. Such amendments must have a proven record of

success and must be certified by the Environmental Protection Agency as posing no

short- or long-term environmental threat. The rate and method of application shall

be that recommended by the manufacturer.

804.3	Preparation

If the area to be developed is infested with bindweed, thistle, or other noxious weeds,

such vegetation shall be eradicated by an application of an effective, environmentally

safe, non-residual herbicide such as glyphosate (Roundup), or approved equivalent, as

approved by the City Engineer. Any chemical which so requires must be applied by an

applicator licensed by the State of Nebraska Department of Agriculture at a rate and

period recommended by the manufacturer. A second application may be required, if the

first application is deemed to be ineffective, as determined by the City Engineer.

Prior to planting, the Responsible Party shall uniformly incorporate the specified

organic soil amendment at the rate of four cubic yards per 1,000 square feet, along

with any reserved topsoil and the specified starter fertilizer as determined by the

soil analysis, to a depth of six inches with a disc, rototiller, or other suitable

equipment. For non-irrigated grass areas, the requirements for soil amendments and

fertilizers may be waived if the soil analysis indicates that such amendments would not

be beneficial to the specified grass mix. All planting areas shall be graded to the

desired finished grades within a tolerance of +/- one-tenth (0.1) of a foot. The

finished surface shall be even and uniform, and no dirt clumps, stones, sticks or

other debris larger than two inches in diameter shall appear on the surface. For non-

irrigated grass areas on sloping ground, the final soil preparation operations shall

be parallel to the general contour. When planted areas are next to fixed surfaces,

such as walks, curbs, or borders, the planted area shall be kept at the following

depths below such surfaces: for seeded areas, 3/4 inch; for sodded areas, 1 1/2

inches; and for shrub and tree beds, four inches.

804.4	Inspections

Refer to subsection 106.3 of these Standards and Specifications.

(a)	Materials Inspection

The Inspector shall inspect all organic soil amendments and fertilizer upon

delivery to the site. The Contractor shall retain delivery tickets for

verification of source, materials, and quantities. Any unsatisfactory materials,

as determined by the Inspector, shall be removed and replaced with materials

conforming to these Standards and Specifications. City inspection shall be both

for quality and quantity of materials.

(b)	Soil Preparation Inspection

The Inspector shall inspect the soil preparation for conformance to the drawings

and these Standards and Specifications during or immediately following the

completion of each segment of the Responsible Party's work. Any work deemed by the

City to be faulty or not in accordance with the approved drawings and these

Standards and Specifications shall be corrected at that time. The following is a

list of the required inspections in their order:

1.	Pre-construction (if not performed prior to rough grading).

2.	Following weed eradication (if not performed prior to rough grading).

3.	Following topsoil stripping and stockpiling (if not performed prior to

rough grading).

4.	During final grading.

5.	After application of organic soil amendments, prior to tillage.

6.	After final grade is completed, prior to seeding and sodding operation.

805	SEEDING SPECIFICATIONS

805.1	General

The Responsible Party shall provide all labor, equipment and materials necessary to

furnish and install seed as required by the approved drawings and these Standards and

Specifications.

805.2	Materials

(a)	Fertilizer

All fertilizer requirements shall be as stipulated in these Standards and

Specifications, subsection 804.2.

(b)	Seed

Seed shall be labeled in accordance with the USDA Rules and Regulations and the

Federal Seed Act. Seed shall be equal in quality to the standards for "Certified

Seed" and shall be furnished in sealed, unopened, standard containers. Seed shall

be fresh, clean, pure live seed. Seed bag tags shall be removed by the City

Inspector following delivery to the site. The calculation of pounds of bulk seed

needed shall be based on the percentage of purity and the percentage of germination.

All seed shall be free of Poa annua and all noxious weeds.

The specific rate, percentage and/or type of seed mix to be applied shall be

subject to the review, revision and approval of the City. Each seed specification

shall be responsive to water conservation concerns, site specific conditions, and

the design intent.

(c)	Wood Fiber Mulch for Seeded Areas

Mulch for seeded areas shall be degradable, non-asphaltic based, green-dyed

cellulose fiber or 100 percent recycled long fiber pulp, free from weeds or foreign

matter toxic to seeds, and suitable for hydromulching.

(d)	Tackifier

Tackifier material shall be an organically-based material compatible for use with

specified seed and/or hydromulch. The tackifier shall not inhibit plant growth

and shall effectively bind mulch material to the soil until the plant material

is established.

805.3	Process

(a)	Drill-Seeding

Wherever slopes can be safely negotiated and soil conditions permit, seed shall

be applied using a Brillion seeder or equal equipment to drill the seed into the

seedbed. The drill shall be equipped with a satisfactory feeding mechanism, an

agitator, double disc furrow openers, depth bands and packer wheels. Seed shall

be sown to a depth recommended by the seed distributor. Where slopes allow,

seed drilling shall be done in two separate applications crossing the area at

right angles to one another to assure proper coverage.

(b)	Broadcast Seeding

In areas where drill seeding cannot be used, a broadcast method may be substituted,

if approved by the City. If the broadcast method is used, the seeding rate shall be

doubled from that recommended for drill-seeding. All seeded areas shall be lightly

raked and rolled after seeding.

(c)	Temporary Seeding

Areas which have been overlot graded but which shall remain undeveloped for a

period of six months or longer or are subject to erosion shall be seeded with an

annual grass seed mix, using the appropriate method as described above. If

disturbed land remains undeveloped for more than one year, reapplication of

annual grasses (or use of perennial grasses) may be required.

(d)	Mulching for Seeded Areas

During hydroseeding, (or following drill-seeding), seeded areas shall be

protected from erosion by hydraulically applying the specified mulch over all

seeded areas, at the rate of 46 pounds of wood fiber per 1,000 square feet, or

2,000 pounds per acre, with the specified tackifier applied concurrently at

60 pounds per acre, or as recommended by the manufacturer.

(e)	Seeding Seasons

For non-irrigated grasses, the spring seeding season shall be spring thaw to

May 15. The fall seeding season shall be from September 15 until consistent

ground freeze. For irrigated grasses, the seeding season shall be March 15 to

September 15.

805.4	Cleanup and Maintenance

All ground area disturbed as a result of seeding operations shall be renovated to its

original condition or to the required new appearance.

805.5	Inspections

Refer to subsection 106.3 of these Standards and Specifications.

(a)	Inspection of Seed Certifications

Seed certification tags shall be removed by the Inspector to verify compliance with

these Standards and Specifications.

(b)	Germination Inspection

When germination is complete and plants are visible, the Responsible Party shall

notify the Inspector and request a germination inspection. Germination shall be

deemed acceptable when the following occurs:

Irrigated Seed:         When all seed areas have a uniform grass growth and

where scattered bare spots not greater than one square

foot do not exceed 10 percent of the areas seeded.

Non-irrigated Seed:     When all seed areas have evidence of germination and

strong growth and where scattered bare spots not greater

than one square foot do not exceed 20 percent of the area

seeded. Seed bag tags shall be used to help substantiate

that appropriate seed quantities have been applied.

All washouts shall be regraded and reseeded immediately after the germination

inspection. No partial acceptance shall be made.

All seeded areas that do not have a uniform germination by September 30 shall not

be accepted by the City until the following spring when the criteria stated above

have been met.

805.6	Warranty

Refer to subsection 106.4 of these Standards and Specifications.

806	SODDING SPECIFICATIONS

806.1	General

The Responsible Party shall provide all labor, equipment and materials necessary to

furnish and install all sod as required by the drawings and these Standards and

Specifications.

806.2	Materials

(a)	Fertilizer

All fertilizers shall be as stipulated in these Standards and Specifications,

subsection 804.2.

(b)	Sod

Selected grass varieties shall be appropriate for site conditions and intended

use, while also responding to water conservation concerns; the grass mix shall be

subject to the review, revision and approval of the City Engineer.

Sod shall have a vigorous and healthy root system and top growth and shall be free

of insects, noxious weeds, undesirable plants, roots, stones, and other foreign

materials which shall be detrimental to proper development of the sod. Sod shall

have been regularly fertilized, watered, mowed and sprayed. The sod shall be mowed

to a height not to exceed two inches and thoroughly watered before the lifting of

the sod. All sod shall be cut to provide a minimum thickness of 3/4 inch of soil

adhering to the roots. Each sod strip shall have a minimum width of nine inches

and a minimum length of 24 inches. The Responsible Party shall furnish written

proof of sod variety to the City Engineer. Sod must be tested by a local extension

agent or a certified laboratory at the Responsible Party's expense if requested by

the City Engineer.

806.3	Process

(a)	Care and Handling

Care shall be exercised at all times to retain the soil on the sod roots during

transportation, handling and planting. Dumping sod from vehicles shall not be

permitted. The sod shall be transported within 24 hours from the time it is cut,

unless it can be stored to the satisfaction of the City Engineer. During delivery

and while in stacks, all sod shall be kept moist and protected from air exposure,

sun and freezing. All damaged sod shall be rejected.

(b)	Transporting Sod On-site

Sod can be transported on or across the site on pallets by forklift. Damage to the

sod bed by the vehicles shall be kept to a minimum; any damage shall be repaired

to the satisfaction of the City prior to sodding of the area. Damage caused to

paving, curbs, fences, plants or other objects from sodding operations shall be

remedied by the Responsible Party at his expense, as directed by the City Engineer.

(c)	Sodding

The Responsible Party shall lightly irrigate the sod bed just prior to laying the

sod. All sod strips shall be placed tightly against each other so that no open

joints are apparent. Joints between ends of strips shall be staggered at least

one foot between adjacent rows. Along walks, drives and curbs, the sod thatch

shall have a finished grade 3/4 inch below the abutting surfaces. Sod placed in

drainage swales or on slopes greater than three horizontal to one vertical

shall be staked, with stakes spaced not more than 30 inches apart, driven into

the ground at an angle against the flow of the water until the top of the stake

is three inches above the sod. All stakes shall be removed prior to mowing.

Sodding shall begin at the bottom and progress upward with strips laid

perpendicular to the flow of the water. Immediately after the sod has been laid,

it shall be rolled with approved equipment to eliminate all air pockets and to

provide a smooth and even surface of the sodded areas. Immediately after rolling

the sod, sufficient water shall be applied to saturate the sod completely. The

sod shall be protected from drying and shall be watered as often as required.

Settled sod areas shall be pulled, regraded, and relaid.

806.4	Cleanup and Maintenance

Any excess debris, peat, soil, or other material which has been brought onto the

project site shall be removed. All ground area disturbed as a result of sodding

operations shall be renovated to its original condition or to the required new

appearance.

806.5	Inspections

Refer to subsection 106.3 of these Standards and Specifications.

806.6	Warranty

Refer to subsection 106.4 of these Standards and Specifications.

807	PLANTING SPECIFICATIONS

807.1	General

These planting specifications cover the installation of trees, shrubs and ground

covers. The work to be performed consists of installation of all plants, including

the furnishing of all materials, equipment, supplies, labor and transportation to

the site. All work shall be performed under the direct supervision of an experienced,

qualified superintendent.

807.2	Materials

(a)	Geotextile Fabric

All shrub beds mulched with inorganic material (rock cobble, etc.) shall include

a geotextile fabric approved by the City Engineer. The fabric shall be installed

below the mulch covering.

(b)	Mulch

All tree wells and shrub beds shall be covered with a mulch approved by the City

Engineer. Wood mulch is preferred, although rock mulch may be allowed in limited

areas.

(c)	Staking and Guying Materials

All trees shall be staked and guyed using the following materials:

1.	Stakes: Deciduous trees -- six to eight-foot long green steel tee posts.

Evergreen trees -- two-foot long steel tee posts.

2.	Wires: Number 12 gauge galvanized wire.

3.	Nylon straps with brass grommets, properly sized and designed to withstand

anticipated loads.

4.	Wire guys shall be flagged with ribbon in pedestrian areas.

(d)	Plant Materials

All selected plant material shall be subject to review, revision and approval by

the City Engineer.

The Responsible Party shall furnish and install all plants shown on the approved

drawings.

All plant material shall conform to the standards of the American Association of

Nurserymen (AAN), as published in the current edition of "American Standard for

Nursery Stock" (ANSI Z60.1-1980). Trees that exhibit signs of mechanical injury,

girdled roots or crushed trunks or root balls shall not be accepted. All trees

shall be well-branched; trees of the same species planted in groups shall be

well-matched. Unless characteristic of a species, trees with codominant stems

shall not be accepted. Plant material shall be free of disease and insect

infestation and have healthy buds. Evergreen foliage shall have healthy and

intense color. All trees shall be inspected and tagged with a locking tree tag

by the City at the nursery prior to delivery to the site. Trees delivered to the

site without a City locking tree tag may be subject to rejection.

All plant material shall conform to the measurements as noted on the plans approved

by the City. All deciduous trees shall be two inch caliper or larger (measured six

inches above grade for calipers of four inches or less, and twelve inches above

grade for calipers greater than four inches) and evergreen trees shall be a

minimum of six feet in height. Plants larger than specified in the plant list may

be used if approved by the City.

Balled and burlapped plant material shall have a root ball in accordance with AAN

Standards. Balls shall be firmly wrapped with burlap or similar materials and

bound with twine or cord. No balled plant shall be planted if the ball is broken,

either before or during the planting process, or if the plant is rootbound. Any

plant which is loose in the ball shall be removed from the site and replaced with

another plant.

If any plant material is found to be unavailable in the metropolitan area, the

Responsible Party must notify the City Engineer in writing. The City shall select

a comparable substitute plant. Substitutions shall be of the same size, value and

quality as the originally specified plant material.

(e)	Tree Wrap

Tree wrapping material shall be first quality, four inch wide, bituminous

impregnated tape, corrugated or crepe paper, brown in color, specifically

manufactured for tree wrapping.

(f)	Edging Material

Any edging materials used shall be durable, with minimal visual impact (unless

the visual impact of such material is an essential element of a pleasing design).

Painted steel edging, minimum 14 gauge, is generally recommended.

(g)	Fertilizer

Where shown to be needed by the soil analysis, fertilizer shall be applied to all

planted areas. The selection of fertilizer type and rate and method of application

shall be based on anticipated maximum effectiveness in aiding plant establishment.

807.3	Process

(a)	Location Staking

The Responsible Party shall stake the proposed locations of all trees and shrubs on-

site for approval by the City Engineer prior to planting. The Responsible Party

shall also arrange to have the locations of all utility lines (including water,

sewer, gas, electrical, phone, cable television, and irrigation) marked prior to

construction to assure safety and protection.

(b)	Delivery/Handling

All plants shall be protected from the time of digging to the time of initial

project acceptance from mechanical injury, excessive drying or winds, improper

ventilation, overwatering, freezing, high temperatures, or any other condition

damaging to the plant. Any plants showing evidence of poor care or which are molded,

mildewed, excessively wilted or dried shall be rejected.

All evergreen plants and deciduous plant material that is in leaf shall be covered

with shade cloth during transportation. Plant material not protected during

transportation may be rejected. Plant material shall be planted on the day of

delivery, if possible. All plants not planted on the day of delivery shall be

placed in a temporary nursery and heeled-in immediately with a mulch and kept

moist.

Plants with root balls that are, in the opinion of the City Engineer, loose,

cracked, broken, man-made or completely dry, or plants with trunks loose in the

root ball before or during planting operations, shall not be accepted. Trees

with branches broken or trunks injured during transportation or planting may be

rejected. Plants that are rejected on site shall be removed within 24 hours at the

Responsible Party's expense.

(c)	Planting

All planting pits shall be excavated to a width that is at least twice the diameter

of the root ball. Sides of the planting pit shall be loosened to avoid glazing. Pits

shall have a flat bottom and be excavated to a depth of two inches less than the

measured height of the root ball for deciduous and spruce trees and all shrubs, and

three inches less than the measured height of the root ball of pine and fir trees.

The base of all root balls shall be placed on undisturbed soil. Plants shall be set

in the center of the pit, plumb and straight. Tress that are not centered or planted

plumb, or have been mechanically straightened, shall be rejected.

All planting pits shall be filled with water prior to planting. All water in the pit

shall be absorbed by the surrounding soil prior to planting. Pits that do not drain

completely within 24 hours shall be provided with a 12 inch diameter, 36 inch deep

auger hole from the bottom of the pit filled with three-quarter inch washed gravel.

All fasteners, containers and wire baskets shall be removed from all tree root balls

in a manner which does not damage the root ball. The method of wire basket removal

shall be to remove the bottom of the basket at the side of the planting pit and to

remove the remainder of the basket once the root ball is centered in the planting

pit. Burlap shall be untied from the root ball and folded back to the bottom of the

planting pit.

Plants in containers shall be removed from the container prior to planting. If the

root system of a container grown plant has become root bound, the roots shall be

gently cut vertically on four sides and on the bottom of the root ball and fanned

out prior to backfilling.

Backfill mixture for tree pits shall consist of two-thirds native soil and one-

third well-rotted organic material, except cow manure (as specified in subsection

804.2(a)), thoroughly mixed. Shrub and/or  ground cover planting beds shall be

amended as specified in subsection 804.3. Any added fertilizer for trees, shrubs,

or groundcovers shall be incorporated at the rate and by the method recommended

by the manufacturer. All plants shall be kept plumb and straight as the pit is

filled with backfill mix. Any plant which is not plumb prior to final acceptance

shall be rejected. For trees in non-irrigated areas, a well three inches in

height shall be formed in a 36-inch diameter circle around the trunk.

All tree and shrub tags shall remain on the plants until the time of final

acceptance. After such time, all tags shall be removed by the City.

The top of all edging material shall be one-half inch above the finish grade of

adjacent lawn or mulch areas.

(d)	Pruning

If directed by the City Engineer, all plant material shall be neatly pruned in

accordance with the best standard practices established by the National Arborist

Association. Each plant shall be pruned to preserve its natural form and character

and in a manner appropriate to its particular requirements. All weak, sharp-angled,

crowded, dead and broken branches shall be removed. All pruning shall be done with

clean, sharp, sterile tools.

(e)	Wrapping

No tree wrapping shall be permitted until the tree has been inspected by the City

Engineer. It is the responsibility of the Responsible Party to wrap deciduous trees

during the one year warranty period. Trees shall be wrapped no later than October 31

of the year they are planted. Wrapping shall begin at the base of the tree,

overlapping on each turn by at least one-half inch and working upward to the lowest

lateral branch. Tree wrap shall be secured with electrical tape at the top and

bottom of the tree wrap and at 18-24 inch intervals, as needed. In no instance shall

staples be used to secure tree wrap.

(f)	Staking and Guying

Tree stakes shall be driven into stable ground and not into disturbed backfill. Two

stakes, oriented northwest/southeast shall be used for deciduous trees; three guy

wires, evenly spaced, shall be used for evergreen trees and very large deciduous

trees. Trees shall be secured to stakes using a properly sized nylon strap with

brass grommets for attachment of wire between strap and stake. Straps shall be of

sufficient length in relation to tree caliper so that grommets do not touch tree

trunk. Wire used to secure the strap shall be galvanized steel and shall be covered

with white one-half inch PVC or other approved material at least 15 inches in

length for visibility and safety.

(g)	Mulching

All tree wells and shrub beds shall be covered with a wood or rock mulch approved

by the City Engineer. Geotextile fabric shall be installed in accordance with the

manufacturer's recommendations below all inorganic (rock, cobble, etc.) mulches. The

mulch shall be spread evenly to a minimum depth of three inches and a minimum

diameter of 36 inches on all trees. Tree wells and shrub beds shall be free of seed

and sod prior to mulching. Wood mulch shall be watered thoroughly at least twice

following installation to aid in matting the mulch.

807.4	Cleanup and Maintenance

All construction debris and surplus materials shall be removed from the project area,

including but not limited to streets and sidewalks, at the completion of each day's work.

Upon completion of the landscape installation, the Responsible Party shall remove all

debris such as rocks, concrete, gravel, containers, wires, ropes, equipment and excess

soil from the site.

807.5	Inspection

Refer to subsection 106.3 of these Standards and Specifications.

807.6	Warranty

Refer to subsection 106.4 of these Standards and Specifications.

808	TREE PRUNING SPECIFICATIONS

808.1	Safety Standards for Tree Trimming and Tree Removal

(a)	Conduct of Operations

The authorization of work on trees neither expresses nor implies a right to violate

any law while in the process of performing such work.

All work shall be performed under the direct supervision of a qualified supervisor.

All such work shall be conducted in a manner as to cause the least possible

interference with, or annoyance to, other persons.

Inadequately or improperly trained personnel shall not be utilized for work on

trees.

Any use of tools or equipment in an unsafe condition or any application of

techniques or methods deemed unsafe to persons or property is forbidden.

Whenever large tree sections are being cut, such sections shall be secured by

ropes and lowered safely in a controlled manner.

Tree workers shall not leave the work site if any severed or partially cut limbs

remain on a tree.

Under no conditions shall the accumulation of brush, limbs, logs, or other debris

be allowed along a public street in such a manner as to result in a public hazard.

Clean up of branches, logs or any other debris resulting from any tree service

operations shall be promptly and properly completed. The work area shall be kept

safe at all times until the clean up operation is completed.

Any injury to persons or damages to any improvement, tree, or structure located

upon or underneath any public street or public right-of-way resulting from any

permitted tree work shall be promptly reported to the City Engineer and

arrangements made to promptly make restitution or repair.

Pedestrian and vehicular traffic shall be allowed to pass through the work areas

only under conditions of safety and with as little inconvenience and delay as

possible.

Prior to the closing of any traffic lane(s), a traffic control plan shall be

submitted to and a permit received from the Traffic Engineer. At least one worker

shall serve to coordinate safe operations on the ground at all times when work

operations are in progress.

Whenever electric, telephone, gas or water lines, or any other public or private

improvements, shall be jeopardized by any authorized tree activity, the Responsible

Party shall consult with the utility company or property Responsible Party involved

prior to any tree pruning. All requested reasonable precautions shall be honored.

(b)	Conditions Requiring Tree Work

Tree work shall be required when a tree poses a hazard to persons or property, as

determined by the City Engineer.

Trees may be removed when age, disease or mechanical injury have so impaired the

tree's ability to survive that harm to persons or property appears imminent.

Trees shall generally be pruned in such a manner as to prevent branch or foliage

interference with requirements of safe public passage. Over-street clearance shall

be kept to a minimum of sixteen feet above the paved surface of the street, and

eight feet over the surface of a public sidewalk or pedestrian path.

All dead, dying or broken branches of two inches or more in diameter shall be

removed promptly.

All branches which are excessively overburdened and appear likely to break shall

be pruned to remedy this condition.

Any limb which extends in an awkward manner beyond the general perimeter of the

tree shall be pruned to restore the shape typical of the tree.

Branch bark ridges and branch collars must be left intact after the final cut is

made. Neither flush cuts nor unsightly branch stubs shall be allowed.

809	IRRIGATION SYSTEMS

809.1	General

All design plans and specifications shall be approved by the City Engineer prior to the

commencement of any irrigation work.

Work shall be performed in accordance with the best standards of practice relating to the

various trades and under the continuous supervision of a competent foreman capable of

interpreting drawings and specifications. The Responsible Party shall notify the City

Engineer as soon as any discrepancies between plans and specifications are discovered.

All surplus material resulting from this Responsible Party's work shall be removed from

the site by the Responsible Party. during this work, the Responsible Party shall keep the

site as clean and free of rubbish as possible.

The Responsible Party shall guarantee all material and workmanship for a minimum period

of one year after the date of initial acceptance by the City.

Work shall include all labor, materials, equipment and appliances as required to complete

the irrigation system as indicated on the approved irrigation plan and as herein

specified. The work shall comply with the City Codes. The Responsible Party shall apply

for all necessary permits as required by the City.

All components of the spray-type irrigation systems shall be designed to adequately

water plant materials only during the period from 10:30 p.m. to 5:30 a.m. Future

expansion shall be anticipated in any design.

For pipe sizing purposes, irrigation and water supply lines downstream from the

backflow prevention unit shall not have velocities exceeding five feet per second.

Spacing of irrigation heads shall be in conformance with the manufacturer's

recommendations. Operations pressure for each head shall be within the limits recommended

by the manufacturer. Pressure at all heads within a single zone should not vary more than

20 percent.

The Responsible Party shall furnish the City with:

(a)	two quick coupler keys and hose swivels

(b)	two drain valve keys

(c)	two manual valve keys

(d)	two control clock keys

(e)	warranty cards on irrigation controller

(f)	equipment manual on booster pumps

All existing utilities shall be located before any excavation work is started.

809.2	Materials

(a)	Water Taps, Meters, and Backflow Prevention Units

All water taps, meters, and backflow prevention units shall be approved by the City

Engineer and shall be installed in accordance with all pertinent City and state

regulations and these Standards and Specifications. The backflow prevention unit

shall be protected by an approved pre-fabricated lockable aluminum enclosure with

viewing ports to allow for inspection of the unit.

(b)	Booster Pump

An evaluation of the existing water main static pressure and the design requirements

of the irrigation system shall be completed to determine whether or not a booster

pump is required. When a booster pump is needed, it shall be a Peerless or approved

equivalent, with magnetic starter and heater. The heater and starter shall be

approved by the City prior to installation.

(c)	Controllers

The irrigation controller shall be UL listed, electrically powered, solid state with

LED, and capable of operating 24 volts electric solenoid zone valves. It shall have

pump start (where applicable), master valve, repeat cycle, dual program, manual

advance, two minute test, battery back up, remote ready, percent scaling, rain

switch, and lightning surge protection features. A rain sensor shall be connected to

the controller. All features shall be approved by the City. The controller shall be

housed in a lockable, manufactured, vandal resistant enclosure approved by the City.

Where necessary to enhance the efficiency of the irrigation system, use of

Motorola MIR 5000 Satellite or approved equivalent controllers shall be encouraged.

(d)	Zone Valves

The zone valves shall be constructed of brass or plastic and shall be operated by a

24 volt solenoid. All valves shall be approved by the City.

(e)	Irrigation Heads

Selected irrigation heads shall perform well under available water pressure.

Irrigation heads installed in large areas of turf grass shall be a gear-driven

rotor type approved by the City. The Responsible Party shall provide rubber covers

for installation on athletic fields. Spray heads installed in smaller turf areas

shall offer a matched precipitation rate between full circle and partial circle

coverages. The heads shall have a three to six inch height of pop with a

retraction spring. Low volume spray heads (using a six to 12 inch pop-up along

walks or fixed risers or pop-ups elsewhere), bubbler heads or drip emitters shall

be used in shrub and flower beds.

(f)	Electrical Wire (24 volt)

All conductor connections to the solenoid on the valve shall be made with a

waterproof 3M DBY or Geltite type connector, or approved equivalent. The control

wire shall be 14 gauge UF single strand, direct burial solid copper wire with

the insulation being a consistent color throughout the entire wire. All lead wire

insulation shall be a solid color (red, orange, black) with the common conductor

insulation being white. Two extra striped insulated wires shall be provided to the

farthest valve on each mainline branch.

(g)	Pipe

All pipe shall be continuously and permanently marked showing the manufacturer's

name, the size, and the class of the pipe. All pipe shall conform to the

requirements of ASTM-D-2241.

1.	All main line pipe shall be Class 200 PVC.

2.	All lateral line pipe of one-half inch or larger shall be Class 200 PVC or

100 pound NSF polyethylene.

3.	All solvent welded fittings shall be Schedule 40 PVC. All threaded fittings

shall be Schedule 80 PVC.

4.	Polyethylene pipe must be NSF approved and shall be allowed in drip systems.

All clamps shall be stainless steel.

5.	Piping from lateral lines to irrigation heads shall be connected by approved

swing joints on rotary heads or by flexible pipe on pop-up heads, as approved

by the City. Swing joints shall consist of Schedule 80 PVC nipples (minimum

six inches long) and Schedule 80 PVC threaded elbows or street elbows.

6.	Responsible Party shall use only the solvent supplied and recommended by the

manufacturer to make solvent-welded joints. The pipe and fittings shall be

thoroughly prepared before applying solvent. The manufacturer's recommendations

and the best practices of the industry shall be followed when making any pipe

connections.

The Responsible Party is cautioned to inspect the pipe and fittings carefully to

assure conformance with the standards as outlined in these Standards and

Specifications. Fittings and piping that do not have a friction fit before the

pipe "bottoms" into the fitting shall NOT be accepted under the terms of the

Responsible Party's work. Rejected pipe and fittings shall be removed from the site

daily to prevent accidental use of this material.

(h)	Quick Coupler Valves

Quick coupler valves shall have a brass two-piece body for a working pressure of

150 psi, operable with a quick coupler key. The quick coupler valve shall be

equipped with a rubber cover and located in an approved 10 inch round valve box.

Key size and type shall be shown on plans. Quick coupler valves shall be located

along the mainline as designated on the plans approved by the City.

(i)	Stop and Waste Valves

An approved stop and waste valve shall be installed between the meter and the

backflow prevention device and shall be installed per City Code. All stop and waste

valves shall discharge into a sump which shall contain a minimum of three cubic

feet of three-quarter inch washed rock overlying an approved geotextile fabric.

(j)	Manual Drain Valves

An approved manual drain valve shall be installed at all low points along the

mainline. All manual drain valves shall discharge into a sump which shall contain

a minimum of three cubic feet of three-quarter inch washed rock overlying an

approved geotextile fabric.

(k)	Isolation Valves

Isolation valves approved by the City shall be placed along the main line.

Placement shall be determined by the City and shown on the approved plans.

(l)	Valve Boxes

All valves shall be installed in valve boxes approved by the City.

809.3	Site Conditions/"As-Builts"

The Responsible Party shall coordinate the work with that of other trades wherever

possible so as to prevent conflicts; this shall include coordination of all sleeving,

in order to avoid future site disruption. Before starting work, the Responsible Party

shall inspect the site and check all existing conditions to ensure that the work may

safely proceed. Before proceeding with any work, the Responsible Party shall carefully

check and verify all dimensions.

Changes or alterations in the system to meet site conditions shall be made at the

Responsible Party's expense. If any work is installed in locations other than shown

in the accompanying irrigation plan, the Responsible Party shall draw on the "As-

built" plans the exact location of those changes. Exact measurements of buried valves

and wire locations shall be shown. The Responsible Party shall present the "As-built"

plans, on a reproducible mylar, to the City prior to initial acceptance.

The Responsible Party shall be responsible for all costs incurred for supplying the

electrical needs required for the job. The electric utility supplier should be contacted

for information on possible electrical sources.

809.4	Excavation

All pipe shall be installed in a trench. Trenches shall be dug true to the alignments

shown on the approved plans. Excavation of the trenches shall be done in a workman-like

manner, resulting in a trench that is straight and true with a flat bottom, and

containing no rocks or other deleterious material that may damage the pipe.

No trench shall be left open overnight without specific prior approval by the City.

Sufficient barricades to protect the public shall be provided at all times, as needed.

809.5	Process

Prior to excavating or trenching, the Responsible Party shall stake all proposed and

existing utilities and all irrigation head and line locations. Stakes shall be suitable

wooden stakes color-coded for materials and shall be maintained throughout the irrigation

installation process.

Separate trenches shall be dug for each line; no doubling up of lines in a single trench

shall be allowed. Trenches shall be of sufficient depth to allow the following cover over

the top of the pipe:

Lines                       Minimum Cover to Top of Pipe

Laterals                               12 inches

Mainline                               18 inches

All mainline three inches or greater shall have appropriate concrete thrust blocks at

all bends, tees, or crosses.

Control valves shall be installed with the top of the valve stem six inches below grade

and covered by a valve box extender to bring the cover of the box to the finished grade.

All zone valves shall be placed in valve boxes. Bottom of valve boxes shall be lined with

a geotextile fabric approved by the City, a minimum of four inches of gravel shall be

placed on top of the approved fabric. The valve box shall be centered over the valve to

provide adequate accessibility. A service loop twice the depth of the buried wire shall

be coiled and placed inside the valve box. The coil shall be made by tightly wrapping the

control wire around a one-half inch piece of PVC, then removing the PVC pipe and placing

the coil inside the valve box.

Whenever possible, the electrical valve control wires shall be buried under and to one

side of the main line. Where more than one wire is placed in a trench, the wires shall be

bundled together at twelve foot intervals. Only 3M DBY or Geltite type connectors or

approved equivalent shall be used in making wire connections; all connectors must be

within a valve box. All wire shall be kept deep enough to maintain a minimum cover of 24

inches when not along the main line and shall have a yellow, six-inch wide warning tape

placed 12 inches above all wiring.

All trenches shall be inspected prior to back filling.

All backfill material shall be free of rocks one inch in diameter and larger. Backfill

material shall be compacted to 90 percent of maximum dry density in accordance with

ASTM D698 Standard Proctor Method. No trench shall be backfilled until it is inspected

by the City.

Backfill shall be tamped under the irrigation head flange and around the head for a

distance of one foot by a suitable means.

Prior to head installation, all pipe lines shall be flushed with water. Install heads,

being careful not to get dirty water or debris in the riser. All sprinklers shall be

checked for the proper operation and proper alignment for direction of throw.

After the system is thoroughly flushed and ready for operation, each zone of sprinklers

must be tested to insure proper operations pressure at the farthest head on the zone

(refer to subsection 809.6(d)).

809.6	Inspections

Refer to subsection 106.3 of these Standards and Specifications.

(a)	Irrigation Location Staking

The City shall inspect the staked locations of all lines and heads for conformance

to the approved plans and these Standards and Specifications. The City reserves the

right to move, shift, and adjust any of the stakes, with the designer's concurrence,

to better achieve the design intentions as shown on the approved plans. No trenching

shall be done until the inspection is complete and the staked locations are approved

by the City. No partial acceptance shall be made.

(b)	Main Line Pressure Test Inspection

The City shall inspect the depth of pipe joints, all joints, stop and waste valves,

manual drain valves, sumps, control valves and solvent welds for conformance to the

drawings and these Standards and Specifications before they are buried. A pressure

test shall be conducted at 120 psi or 40 psi over static pressure, whichever is

greater, for a period of two hours to ensure that the system is watertight.

(c)	Wiring Inspection

Once the wiring has been installed, the City shall inspect it for conformance to

the approved plans and these Standards and Specifications. No partial acceptance

shall be made.

(d)	Coverage and Pressure Test

After the irrigation heads have been installed and backfilling operations are

complete, the Responsible Party, in the presence of the City, shall perform a

coverage test to the satisfaction of the City, ensuring that there is complete

and uniform coverage. The pressure at all heads and valves shall meet

manufacturer's requirements. The pressure within a zone should not vary more than

20 percent among all heads. No partial acceptance shall be made.

809.7	Warranty

Refer to subsection 106.4 of these Standards and Specifications.

810	RECREATION FACILITIES

810.1	General

The design of all recreational facilities, including but not limited to athletic fields,

swimming pools, tennis courts and playgrounds, shall be reviewed and approved by the City

on a case-by-case basis. Construction of any recreational facilities to be owned or

maintained by the City shall not begin without plan approval by the City. In addition,

the following standards shall apply to recreation facilities where applicable:

810.2	Playgrounds

1.	All playgrounds shall comply with the Consumer Product Safety Commission

Technical Guidelines for equipment and surfacing.

2.	All playground equipment shall be installed in conformance with manufacturer's

recommendations by an installer possessing demonstrated skills in playground

installation.

3.	All playground areas shall be separated from adjacent grass or park surfaces by a

concrete or wood edge approved by the City Engineer.

4.	All playground areas shall be provided with a subsurface drainage system

sufficient to adequately drain the playground area. Playground drains shall be

conveyed to storm drainage systems or shall be suitably daylighted in a non-

obtrusive area.

810.3	Athletic Fields

All athletic fields, including but not limited to football, soccer, and baseball fields,

shall comply with the following general requirements:

1.	All slopes or fields shall be uniform. Significant grade breaks in field area shall

not occur.

2.	Slopes of fields shall not exceed 1.5 percent unless approved by Parks

Superintendent and a variance request is submitted to the City Engineer.

3.	Play area of fields should not overlap with use areas of other activities.

4.	There shall be safety areas of sufficient width outside of athletic fields to

promote safe use. Berming or fencing outside of play areas may be required to

prohibit errant balls from traveling to adjacent roadways or property.

810.4	Tennis Courts

Tennis courts designated for City ownership or maintenance shall conform to the

following minimum construction standards:

1.	Tennis courts located on non-expansive soils shall have a base of asphalt laid over

structural backfill or a base of post-tensioned concrete.

2.	All tennis courts shall have an all-weather, non-fading, glare-free strongly bonded

surface finish. Paint shall not be permitted as a surface finish.

810.5	Trails and Sidewalks

All trails and sidewalks constructed within the the City which will be dedicated to the

City for ownership or maintenance shall comply with the following minimum standards:

1.	No trail or sidewalk slopes shall exceed 12 horizontal to one vertical. Sharp grade

breaks will not be allowed. Stairs will not be allowed except where alternative

ramps with acceptable slopes are located in close proximity.

2.	All trails and sidewalks shall be constructed on natural sub-grade, compacted to

95 percent standard proctor density.

3.	All trails and sidewalks shall have a cross slope of one-quarter inch of slope

per one foot of width to allow for proper drainage.

4.	All multiple use trails shall be a minimum of 10 feet in width unless otherwise

approved by the City Engineer. Narrower trails and sidewalks may be permitted as

approved by the City Engineer.

5.	All trails and sidewalks shall be constructed of concrete unless otherwise approved

by the City Engineer. Concrete shall be a minimum of five inches, and shall be made

of concrete with a compressive strength of 4,000 psi at 28 days. All concrete

control joints shall be saw cut; trowel joints may be allowed. Concrete surfaces

shall receive a medium broom finish with the direction of broom strokes being

perpendicular to the length of the trail.

6.	Asphalt surface trails shall be allowed only in unique situations approved by the

City Engineer and shall be constructed in accordance with a soil engineer's

recommendation for the proposed use, location and soil type.

7.	In rural areas, alternative trail materials such as crushed rock may be allowed in

unique situations.

810.6	Recreation Facility Lighting

Lighting shall be provided for recreational facilities and trails, as follows:

1.	Playgrounds: A minimum of one fixture per playground shall be required. More

fixtures may be required if warranted by safety concerns.

2.	Trails: One fixture shall be required at each at-grade trail intersection with a

public or private street. In addition, one fixture shall be required along each

500 lineal feet of trail or sidewalk. In rural areas, exceptions to these

requirements may be granted by the City Engineer.

3.	Parks: Lighting shall be provided in all parks as needed for safety considerations.

Lighting for recreational uses may be permitted, provided that concerns of any

nearby residents are adequately addressed.

4.	All lighting shall be provided by the electric utility supplier at the Responsible

Party's cost. All light fixtures shall be rectangular in shape, with a bronze

anodized finish using a 100 watt HPS light source, mounted on an 18-foot pole,

unless otherwise required.

All exterior lighting will follow the procedure as shown in section 707.5 Street Lighting

Procedure.