# TOP Server Release Notes (5.5.98.0) March 2, 2011

Drivers

Allen-Bradley ControlLogix Ethernet

- Fixed an issue introduced in V5.5.94.0 that affected communications with MicroLogix 1100 controllers, resulting in CIP Error=0x08, Ext. Error=0x0000.

# TOP Server Release Notes (5.5.94.0) February 18, 2011

### Runtime Interface

- Modem functionality has been enhanced to support auto-dialing and improved phone number management.

- Fixed an issue where driver communications could be interrupted by virus scans or other processes that block access to the hard drive.Fixed an issue wherein project backup was being created whenever the startup project was used.

- Added text to the server’s administration “Runtime Process” property page clarifying that DCOM settings do not persist when the Process Mode is changed from System Service mode to Interactive mode.

- Fixed an issue where a runtime failure could occur when an OPC DA client attempts to use the IOPCAsyncIO2 interface without first setting up a data callback.

### Configuration Interface

- OPC Diagnostics will no longer be stopped when a project is uploaded or downloaded between the server configuration and the server runtime.

- A new Multiple Tag Generation tool was added to help users add a large number of tags into the server database quickly. This feature is can be accessed via the “Tag Properties” page.

### Native Client Interfaces

OPC DA Server Interface

- Fixed an issue where an incorrect value was being returned from IOPCServer::GetErrorString() following the successful loading of an expected string. This issue caused the server to fail the OPC DA 2.05 compliancy test.

- The timing settings located in the “OPC DA Settings” Project Properties tab now correctly check for and disallow out-of bound values.

- A new OPC compliancy setting has been added. When set True, it will cause the server to return S_FALSE in the item error array for items that have non-good quality. The new setting defaults to True for existing projects that are set to full compliance, and False for those that are not. When set False, the legacy behavior of returning E_FAIL (0x80004005) will occur.

- Fixed crash uncovered during interoperability testing with COGENT’s OPC DataHub.

OPC UA Server Interface

- Added support for two-dimensional arrays.

- The server now returns a Discovery Endpoint that most closely matches the client’s request, allowing clients to browse the UA server from different subnets.

- Fixed an issue where if secure channels were checking for timeouts while a new secure channel was being opened then a deadlock could occur.

- Fixed an issue where items being added and removed rapidly by a client could cause a deadlock.

- Improved read and write performance by caching items between client calls. Users can now specify the amount of time that a server item is cached via the 'Tag Cache Timeout (s)' setting in the OPC UA Project Properties

NIO Interface

- Fixed an issue where dynamic item references from iFIX that were not using the "@datatype" identifier would not fallback to their default data type in the server.

OPC .NET 3.0 (Xi) Server Interface

- Renamed “OPC Xi” (OPC Express Interface) to “OPC .NET” in accordance with the name change set by the OPC Foundation.

- The OPC .NET (Xi ) service will now shut down if all COM clients disconnect  from a server that is running in Interactive mode.

- Fixed an issue where a server start up delay occurred when the runtime was started with OPC .NET enabled.

- Improved the server shutdown time when no OPC .NET clients are connected.

- A new event log warning message was added to let users know that the service timed out when attempting to start.

### Components / Utilities

PingItFirst Utility

- A new utility was added to help troubleshoot network connection problems with Ethernet devices.

OPC UA Configuration Manager

- The server can now register with multiple Discovery Servers.

- Users will now be warned when importing an expired Instance Certificate.

- Certificates with expiration dates beyond 12/31/2039 are no longer flagged as expired.

- Added support for certificate validation when importing or trusting certificates.

### Plug-ins

Advanced Tags

- Fixed an issue where the Derived Tag dialog partially closed when the Escape key was being pressed and the expression edit control was in focus.

- Added support for CSV import/export.

- Link Item dead values can now be disabled.

- Advanced Tags can now be read when inactive.

SNMP Agent

- The new SNMP Agent Plug-In allows server items to be mapped to SNMP OIDs and polled by SNMP managers on the network. The SNMP Agent can also monitor server items to send event notifications (traps) to network management systems (NMS).

Alarms & Events

- The Multi-Level condition’s LO_LO sub-condition now has a higher priority than LO.

DataLogger

- Fixed an issue where synchronous writes to a device tag would fail after writing to a Log Group’s _Enabled tag.

- Fixed an issue where initial values were not written to the database for the 'Log on Data Change' and 'Log on Static Interval' trigger modes.

- Fixed an issue where log items were using device timestamps to signal data change events instead of the time that the update was received.

- For the Expression trigger Type, users will now be warned if using the Start Condition 'Item has not changed over a certain time period' and the trigger rate is less than twice the tag update rate.

- The Wide Table insertion count now only updates when an insertion succeeds, and only updates once per insertion.

Drivers

Allen-Bradley ControlLogix Ethernet

- Added support for RSLogix Version 19

- Added a new check box setting in the Logix Options page of the driver called “Automatically Read String Length”.  When unchecked, string reads will be optimized  by having the driver bypass the LEN member read and terminate the DATA string at either the first null character encountered or the maximum string length of DATA (whichever occurs first).

- Beginning with L7x controllers, an optimization in controller memory restricts that memory cannot be accessed on a non-DWord boundary or a controller fault will occur. Because the driver was not aware of this restriction, it was possible it could fault the controller while performing Physical reads or writes. To address this issue, the driver now identifies the controller and makes the proper Physical memory access.

- Fixed an issue where tags stopped updating under certain PC environments running a multi-core CPU.

Allen-Bradley DH+

- Enabled Bit support in SLC500 for Counter Status Word.

- Fixed an issue with LBCD ARRAY writes.

Allen-Bradley Slave Ethernet

- The driver will now check for License Activation upon receiving unsolicited communications.

BACnet IP

- Fixed an issue where tags have bad quality if the response to a ReadPropertyMultiple command has multiple properties listed under a single object identifier.

- Added support for discovering devices on a BACnet network.

DNP Master Ethernet

- Enhancements for Phase II support of WITS specification include the following.

  - Added support for writing to Device Attributes (Object Group 0). This feature is required to meet the DNP WITS standard.

  - Added support for writing to Data Sets (Object Group 87). This feature is required to meet the DNP WITS standard.

- The driver now supports the ability to play back Data Set snapshot data.

- New settings were added to the Device Properties page that allow for users to ignore forced flags when setting quality.

- Fixed issues with loading legacy server (.xml) project files.

- Fixed an issue where the first buffered event after startup was never displayed when the Playback Rate was shorter than the tag’s Update Rate.

- A “Device Not Responding” message will no longer be reported in certain situations where the device was actually communicating.

  - Added Event Log error messages for cases of incomplete or invalid responses or invalid authentication.

- Fixed an issue where the driver was reporting “Failed to initialize communication stack” in situations where serialization was enabled.

- Improved channel management when communication errors are encountered during startup.

- Fixed an issue where data set CTLS and CTLV element types were shown as having bad quality.

- Fixed an issue where Communication Serialization and Aggressive Mode Authentication were enabled.

- Added informational message to report the number of data set tags per data set added during auto tag generation.

DNP Master Serial

- Enhancements for Phase II support of WITS specification include the following.

  - Added support for writing to Device Attributes (Object Group 0). This feature is required to meet the DNP WITS standard.

  - Added support for writing to Data Sets (Object Group 87). This feature is required to meet the DNP WITS standard.

- The driver now supports the ability to play back Data Set snapshot data.

- New settings were added to the Device Properties page that allow for users to ignore forced flags when setting quality.

- Fixed issues with loading legacy server (.xml) project files.

- Fixed an issue where the first buffered event after startup was never displayed when the Playback Rate was shorter than the tag’s Update Rate.

- A “Device Not Responding” message will no longer be reported in certain situations where the device was actually communicating.

  - Added Event Log error messages for cases of incomplete or invalid responses or invalid authentication.

- Fixed an issue where the driver was reporting “Failed to initialize communication stack” in situations where serialization was enabled.

- Improved channel management when communication errors are encountered during startup.

- Fixed an issue where data set CTLS and CTLV element types were shown as having bad quality.

- Fixed an issue where Communication Serialization and Aggressive Mode Authentication were enabled.

- Added informational message to report the number of data set tags per data set added during auto tag generation.

Fisher ROC Plus Serial

- Fixed an issue with unhandled exception in the driver .

Honeywell UDC Ethernet

- Fixed an issue where the driver would respond with an error because it was it attempting to read coils on a UDC2500 model that supported less than 8 coils.

Modbus TCP/IP Ethernet

- Fixed an issue with unsolicited connections management and expanded the maximum unsolicited socket connections from 32 to 256.

- Added a setting that allows users to select whether the driver will close the socket on timeout .

- The driver will now check for License Activation upon receiving unsolicited communications.

Modbus Slave RTU Serial

- The driver will now check for License Activation upon receiving unsolicited communications .

OPC DA Client

- Added support for two-dimensional arrays.

OPC UA Client

- Added support for two-dimensional arrays.

- Added support for Certificate Validation when importing or trusting certificates.

Siemens TCP/IP Slave Ethernet

- The driver will now check for License Activation upon receiving unsolicited communications.

SNMP

- Fixed an issue where changing from v2c to v1, the “GetBulk” check box selection was not being persisted.

- Fixed a host name resolution  issue where the driver was no longer receiving SNMP Traps from a device after the device’s IP address changed.

- Added the ability to invalidate rather than deactivate tags that receive "NoSuchInstance" and "NoSuchObject" errors from a device agent.

- Added support for SNMP V3 including Authentication and Encryption of SNMP messages (SNMPv3 security).

Telemecanique Uni-Telway Slave

- The driver will now check for License Activation upon receiving unsolicited communications.

UCON (User Configurable)

- The driver will now check for License Activation upon receiving unsolicited communications .

Yaskawa MP Ethernet

- Added support for the Yaskawa MP2000IEC device series.

# TOP Server Release Notes (5.4.135.0) November 2, 2010

### Installation Fixes

# Modified the 5.4.131.0 install to respect the run as a service or interactive setting of previous configuration.

# Uninstalling or upgrading version 5.4.131 removes the TOP Server DCOM settings, so upgrading to version 5.4.135 or above will require resetting your TOP Server DCOM settings if you have version 5.4.131 installed.

See next page for other 5.4 release notes enhancements.

# TOP Server Release Notes (5.4.131.0) October 28, 2010

### Runtime Interface

- Modified the server to post a message whenever the Licensing Service is not detected.

- Fixed an issue with copying and pasting devices on a driver that does not allow duplicate Device IDs.

- Fixed an issue wherein project backup was being created whenever the startup project was used.

- Plug-in tags are now included in the project tag count.

- Fixed an issue wherein clients were unable to reconnect to the server via SuiteLink/FastDDE after the server was reinitialized.

- Added check to project loader. This suppresses a warning message from being posted for a missing Advanced Tag plug-in if advanced tags data was not loaded.

- Set the default DCOM access permissions to the same for both Service and Interactive Mode. Previously, it was Interactive User, Self, and SYSTEM for Service Mode only. Now, Built-in Users and SYSTEM is for both. Note: Built-in Users includes Interactive User.

- This update also eliminates the warning message produced from DCOMCNFG concerning invalid permissions (such as when an attempt is made to edit the access permissions that were set when the service was originally registered).

### Configuration Interface

- Fixed an issue wherein menu text was missing in Channel Diagnostics if a modal window was also open.

- Previously, both Import and Export CSV did not suggest a file name when the device or group contained a space. This was fixed by adding logic to accepted spaces, as well as the "-", and by automatically filling the file name for alphanumerics, digits, and the following special characters: ^&'@{}[],$=!-#()%.+~_

- The last viewed tab in the Tools | Options dialog now persists independently of how the window is closed.

- The size of the driver information dialog was decreased and made resizable.

- Added a check to the Device Wizard ID pages to make sure a new device can be added.

- Fixed a crash issue when property pages are open and a new project is loaded by double-clicking on an .opf project file. Now, users cannot load a new project if a modal dialog is currently open.

- Increased the text limit of the Numeric ID edit box to 6 digits in order to support the largest octal value that fits in a word. The width of the edit box was also increased in order to fit the new digit limit.

- Fixed an issue wherein the Alias Import/Export file dialog did not remember the last used path.

- Fixed issue of errors when deleting Advanced Tags when some are referenced and some are not. The Advanced Tag list has been updated.

- Added an option to the View menu to show/hide plug-in tabs. Plug-ins

Server Eventlog

- Added message pump for Third-Party applications that call SendMessageTimeout ().

### Native Client Interfaces

OPC AE Server Interface

- Fixed an issue with copying the condition acknowledgement comment. The problem occurred when an AE client requested the state of a condition.

- Refresh events are no longer sent for inactive, acknowledged conditions (see OPC AE 1.01 specification page. 85).

- Fixed the logic used to compare a client's filter with an event type, thus allowing the filtering on multiple Event types to be handled correctly.

OPC UA Server Interface

- Modified the interface to allow clients to authenticate when anonymous login is disabled.

- Added a new DWord constraint that sets the Min/Max Session Timeout based on server defaults rather than the high/low end of the allowable range. This constraint was also applied to Max Client Sessions.

- The Min/Max Session Timeout is now based in seconds (rather than milliseconds).

- Modified the interface to pass rejected certificates to the rejected certificate directory and post a message to the Event Log.

OPC Xi Server Interface

- Added (beta) support for the OPC Express Interface (Xi) standard.

### Components / Utilities

OPC UA Configuration Manager

- Added the ability to import Instance Certificates.

- Fixed failure to show an error message when dropping an already trusted certificate on the Trusted Server page.

- Added export options to the Trusted Client and Trusted Server dialogs.

- Added buttons for trusting and rejecting certificates on the Trusted Client and Server Certificate pages.

OPC Xi Configuration Manager

- This new utility installs with the OPC Xi Server interface.

Quick Client

- Increased the width of the List column in the Add Items dialog. This allows the tag names to remain visible when the fully qualified name is longer than the width of the list.

Application Report Utility

- Increased the width of the List column in the Add Items dialog. This allows the tag names to remain visible when the fully qualified name is longer than the width of the list.

### Plug-ins

Advanced Tags

- Next and Previous buttons now apply changes to the current tag.

- With regard to the Link Tags' “On Value” Trigger Mode, updated strings are now shown in the Comparison dialog to make the list format consistent.

Custom Alarms

- Comparisons are now shown in the Sub-Condition dialog to make the list format consistent.

DataLogger

- The trigger XML load routine now follows the GUI in enforcing the rule that either the Log on Static Interval or Log on Data Change must be set to true.

- Fixed an issue with XML load bug with absolute triggers, wherein the days of the week value was not loading correctly.

- Fixed an issue wherein sessions were not being closed if an error was thrown by the ODBC layer. This resulted in excess connections to the database.

- Fixed an issue wherein Legacy 4x projects with Log on Static Interval unchecked failed to pass schema validation in 5.3. Fixed an issue wherein Legacy 5x projects with Log on Static Interval unchecked failed to display No in the Interval column on the Triggers tab in 5.3.

Drivers

BACnet IP

- Added support for ISO 10646 (UCS-2) and ISO 8859-1 (Latin1) character sets.

- Added a number of object properties to meet the 2008+ BACnet specification, in addition to support for simple array properties (arrays of primitive BACnet data types).

- Increased the maximum number of channels from 32 to 128.

- Added enumerated values and corresponding strings to support approximately forty new BACnet Error codes.

- Added a new error class.

- Fixed an issue wherein tags with a default client access of Read Only could not be set to Read/Write, even if Write access was allowed.

- Addendum “Add-2004-135m” specifies a small change to the way segment ACK timeouts function. Before the change, Addendum timing started at the beginning of the Request window (during which one or more segments were sent). In some cases, this caused unnecessary timeouts for larger window sizes.  Now, the timer starts after the first segment is sent, after all the segments in the window (1 or more) are sent, or after the last segment is sent to the device.

- Modified BACnetNetworkLayer to be able to route COV notifications from a device on a different BACnet network where NPDUs do not contain the source address.  Although the behavior does not appear to meet the BACnet spec, this precedent has been set by the support of other vendors. A channel property was added to enable/disable this setting. It is disabled by default (since it could degrade performance if the BACnet network has a large volume of broadcast messages).

- Modified the driver so that duplicate Device IDs are not allowed on a channel.

- Increased the COV re-subscription interval maximum value from 1 hour to 24 hours.

- Added an option for ALC devices to use a Subscriber Process Identifier (SPID) of 0. ALC devices consider all subscriptions with an SPID of 0 to be 1 subscription.

- Added an option to wait for the device to acknowledge COV cancellations. This prevents the Runtime from shutting down until all COV subscriptions have been cancelled.  Note: In very large projects, this shutdown delay can make the Runtime seem unresponsive.

Beckhoff TwinCAT

- Added support for TwinCAT PLC version 2.9.  The driver now queries the version information to determine what function codes can be used to communicate with the controller.

Contrex Serial

- Fixed an issue with broadcast mode (Device ID of 0) wherein Write tags were not being released properly.

DF1 Serial

- Added NAK handling for the half-duplex and radio modem link protocols. This situation may occur if communicating to a device configured for full-duplex.

DNP Master Ethernet

- Updated the driver to release items more quickly for unresponsive devices, following client disconnect.

- Added Keep-Alive Interval device property to the Communication page as well as an Event Log message to warn the user if loading an XML project discovers a Keep-Alive interval configured for a UDP channel.

- Enhancements for Phase I support of WITS specification include the following.

  - Device Attribute - Object Group 0:

    - Standard Attributes at Index 0 (such as Vendor Name, Product Name, Site Name, Software Version, Hardware Version, Configuration File Names, and Configuration File Version).

    - User Defined Attributes for Index 1 and above.

    - Read Only.

  - Secure Authentication – Object Group 120:

    - Challenge – Response.

    - Pre-shared Update Keys.

    - Aggressive Mode.

    - Session Keys - bidirectional.

    - Security Statistics.

  - Data Sets – Object Groups 85, 86, 87, and 88:

    - Prototypes.

    - Descriptors.

    - Event and Static conditions.

    - Outstation defined data sets.

    - Read Only.

- Added an error message for the situation in which a device's Slave address is a duplicate of another device's Master or Slave address.

- Added an error message for the situation in which a device contains the same Master and Slave address.

- Added the following internal tags:

- _Protocol

- _DestinationHost

- _DestinationPort

- _SourcePort

- _ChannelResponseTimeout

- _IntegrityPollInterval

- _EventClass1PollInterval

- _EventClass2PollInterval

- _EventClass3PollInterval

- _DeviceRequestTimeout

DNP Master Serial

- Updated the driver to release items more quickly for unresponsive devices, following client disconnect.

- Added support for communication serialization.

- Enhancements for Phase I support of WITS specification include the following.

- Device Attribute - Object Group 0:

  - Standard Attributes at Index 0 (such as Vendor Name, Product Name, Site Name, Software Version, Hardware Version, Configuration File Names, and Configuration File Version).

  - User Defined Attributes for Index 1 and above.

  - Read Only.

- Secure Authentication – Object Group 120:

  - Challenge – Response.

  - Pre-shared Update Keys.

  - Aggressive Mode.

  - Session Keys - bidirectional.

  - Security Statistics.

- Data Sets – Object Groups 85, 86, 87, and 88:

  - Prototypes.

  - Descriptors.

  - Event and Static conditions.

  - Outstation defined data sets.

  - Read Only.

- Added an error message for the situation in which a device's Slave address is a duplicate of another device's Master or Slave address.

- Added an error message for the situation in which a device contains the same Master and Slave address.

- Added the following internal tags:

  - _ChannelResponseTimeout

  - _IntegrityPollInterval

  - _EventClass1PollInterval

  - _EventClass2PollInterval

  - _EventClass3PollInterval

  - _DeviceRequestTimeout

GE Ethernet

- Fixed an issue wherein Symbolic Tags were being forced to Read/Write.

GE Focas1 Ethernet

- Fixed an issue wherein all models except the Series 15i had one or more invalid address ranges. This issue was introduced with the addition of CNC status info tags.

GESNP Serial

- Added SNP protocol specific error messages to the driver.

GESNPX Serial

- Added SNP protocol specific error messages to the driver.

Honeywell UDC Serial

- Fixed an issue wherein the driver did not properly reject a response from a Device ID that was different than was sent in the request packet.

Mitsubishi Ethernet

- Resolved issue for native Boolean address types where driver returned “Bad Address” instead of “Bad Type” on first attempt at adding dynamic tag of data type Double.

- Fixed an issue wherein the parser did not accept addresses for X, Y, W, and ZR if the hex component immediately followed the memory type.

Modbus Ethernet

- In a fix carried over from a patch to 4x, fail now tags immediately if the packet can't be transmitted (instead allowing retry logic to execute).

Modbus RTU Serial

- Increased the number of channels from 100 to 256.

ODBC Client

- Fixed an issue with queries wherein the driver failed to read tags if the query included a UNION.

- The EnableMiscellaneousQuerySettings registry setting was broken in 5x due to the separation of the Runtime and Configuration. The registry setting was removed, and the dialog page made visible to all users. A related wizard page was also added.

Omron FINS Ethernet

- Added support for the CJ2 Model.

- Modified the driver to handle the relay error frame when a fatal CPU error is present. The error messages were also updated to include “Main, Sub:” and “Net Addr, Node Addr:” in decimal notation: this should make it easier for users to compare to Device Property settings in the server project.

- Added the reporting of device-level error conditions and detection of network relay error frames. We now output the following error messages instead of posting "Device not responding" messages:

- Network relay error.[Net Addr, Node Addr: '0x00, 0x3A'], [End Code: '0x8302']

- Fatal CPU Unit error.[End Code: '0x0080']

- Non-fatal CPU Unit error.[End Code: '0x83C2']

Omron FINS Serial

- Added support for the CJ2 Model.

- Added the reporting of device-level error conditions and detection of network relay error frames. We now output the following error messages instead of posting "Device not responding" error messages:

- Network relay error.[Net Addr, Node Addr: '0x00, 0x3A'], [End Code: '0x8302']

- Fatal CPU Unit error.[End Code: '0x0080']

- Non-fatal CPU Unit error.[End Code: '0x83C2']

OPC DA Client

- When adding groups, the time bias is now properly initialized to zero. At this moment, this setting is not user-configurable.

- Fixed an issue wherein the initial update was not passed on to client applications.

- Removed the limit that prevented the creation of nested groups with depth greater than 8.

OPC UA Client

- Fixed an issue wherein the initial update was not passed on to client applications.

- Improved the browse code to report a single failure instead of multiple failures per browse request.

- Added support for the browseNext method, allowing clients to browse and import nodes from a server that limits the max returned nodes.

- Fixed a deadband issue wherein we were not correctly passing in the client item handle for the item to which deadband was applied.

- Removed the driver tag address limit of 1024.

- Fixed duplicate browse entries when performing a full refresh through the context menu in the server browser.

Siemens S7 Ethernet

- Modified the driver to support locale-specific multi-byte strings.

SNMP

- Ehanced MIB parsing capabilities by providing the ability to multi-select MIBs for import, and also made the parser more tolerant of minor MIB warnings (syntax or format) that should not prevent import.

- The user is now prompted when a MIB dependency exists in both the repository and the Import target directory.  If the user confirms overwriting, the repository file will be deleted and the target file will be added to the repository.

- Importing a file that is contained in the repository now causes the existing file to be deleted, and the new file added. Before, the old file was not deleted and the two files coexisted.

- Formatting change for user imported MIBs from "UserImported-<file name>" to

- "UserImported-<module name>_<file name>".

- Fixed an issue in the MIB Import tab of Device Properties wherein selecting "Customize" following removal of a module would re-add the previously removed module.

- Added the SNMP GetBulk command in order to read multiple OIDs from individual tables more efficiently. This is a user-selectable device property and is only used for SNMP version 2c.

- Fixed an issue wherein traps with snmpTrapOid varbinds with trailing “.0s” were not handled correctly.

- Fixed an issue with processing trap events from devices that pad the timestamp of the trap event packet with zeros.

U-CON (User-Configurable)

- Fixed issue where projects created in server/driver version 5.3 that used WriteDeviceID and WriteEventCounter commands would fail version comparison and not load the project in 5.4.

- Fixed an issue wherein legacy .opf projects saved as xml would fail to pass schema validation.

- Modified Transaction Editor Write commands, and also added Data destination radio buttons for Read, Write, Scratch, and Global buffers for commands CmdWriteDeviceId, CmdWriteEventCounter, and CmdWriteCheckSum.

- Increased the Device ID value limit from 255 to 65535.

- The Transaction Editor posted an incorrect validation message when creating a Cache Write Value command without a preceding Transmit command.  A Write Data command is required before a Cache Write Value command.  A Transmit command is not required.  Both the validation and error message have been updated.

- Fixed an issue wherein the driver sometimes failed to respect signed data types if the device data format had fewer bytes than the data type. Signed data types would not correctly display negative values.  The driver now always respects whether the data type is signed when converting to and from the device format.

Yokogawa DX Ethernet

- Enabled error message posting for failed write tags from a non-responding device.

- Fixed an issue wherein the driver would not properly release tag references under certain conditions. This resulted in stale tag data, and stopped further updates from being passed on to client applications.

Yokogawa DX Serial

- Removed tag duplication during automatic tag generation.

Yokogawa DXP Ethernet

- Removed tag duplication during automatic tag generation.

Yokogawa HR2400 Serial

- Removed tag duplication during automatic tag generation.

Yokogawa MX Ethernet

- Removed tag duplication during automatic tag generation.

# TOP Server Release Notes (5.3.156.0) August 10, 2010

### Runtime Interface

- No Changes

### Configuration Interface

- No Changes

### Plug-ins

DataLogger Plug-in

- Fixed issue where projects (V4.x and V5.x) were not loading correctly in V5.3.118 when the Log on Static Interval property was unchecked.

### Native Client Interfaces

Wonderware SuiteLink/FastDDE

- No Changes

iFIX PDB Interface

- Fixed issue where the IDS server was not available to select in iFIX 5.1.

UA Server Interface

- Fixed memory leak that occurred when a 3rd party UA Client continually read invalid items.

- Fixed poor performance reported when running projects configured to use multiple subscriptions per session

OPC DA Server Interface

- No Changes

### Components / Utilities

OPC UA Configuration Manager

- Fixed problem managing endpoints across multiple network cards of the same name.

License Utility

- Fixed issue where Transfer Request File was not created correctly for standalone subscriptions.

Drivers

DNP Master Serial

- Enabled support for Binary Output Events.

DNP Master Ethernet

- Enabled support for Binary Output Events.

GE SNP

- Fixed issue where RS tags (R Strings) were not being handled properly resulting in the tags being orphaned.

Modbus RTU Serial

- Increased the maximum number of COM ports (channels) allowed from 100 to 256.

OPC DA Client

- Removed the limit preventing the creation of nested groups with depth greater than 8.

OPC UA Client

- Removed the limit preventing the creation of nested groups with depth greater than 8.

- Fixed issue where driver would consume memory when reading long string values or large quantities of string tags.

Productivity 3000 Ethernet (Automation Direct Suite)

- Resolved read problem with Continuous Booleans and 1D/2D Boolean Arrays whose range do not end on the byte boundary.

# TOP Server Release Notes (5.3.118.0) June 9, 2010

### Runtime Interface

- BCD tag values are now clamped to the max value for their data type.

- Added support for user-specified startup project from any location in the file system.

### Configuration Interface

- Added “Advanced” channel property page and a property called “Communication Serialization: Virtual Network”. The page will not be shown for drivers that do not support communication serialization.

- Added support for auto-generated aliases in the alias map export if "Show auto-generated aliases" option is checked in Alias Map dialog.

- Added support for UTF-8 encoding of CSV import/export files for aliases and tags.

- Removed the 'Contents' and 'Search' menu options from the Help menu and replaced them with ‘Server Help’.

- Added a plug-in help dialog accessible via the main help menu. The dialog is similar in function to the driver help dialog.

- Corrected instance where undo information was not saved when multiple tags were copied and pasted.

- Alias map menu option is now enabled without requiring a device or a channel to exist in the active project.

- Fixed failure to open a project file when double-clicked in Windows Explorer if an instance of the Server Configuration is already running.

- Fixed an issue where the incorrect channel wizard page was displayed when both Ethernet encapsulation and RTS Manual flow control were enabled.

- Added a horizontal scroll bar to the hint box for cases where the length of a hint exceeds the size of the hint box.

- Increased COM ports range from 1-100 to 1-256.

- Fixed issue where “Auto Create” button on the “Database Creation” tab would not work until the “Apply” button was pressed. Changes made on sibling pages are now applied when “Auto Create” button is pressed.

- The server’s Event Log now supports Event Type (Error, Warning, and Information) for the Save-As-Text-file output.  Output file is now UTF-16 encoded.

- A warning message was added to the Alias Name dialog if the alias name matches any of the channel names in the project.

- Added check for wizard page mode before enabling back and next buttons.  Without the check, the cancel button was the default button in property sheet mode.

- The configuration client now waits a maximum of 30 seconds for the runtime to initialize (this was originally set at 10 seconds).  This extra time will help prevent connection timeouts from occurring when the runtime is either starting on a slow machine or loading a large project.

### Plug-ins

Alarms & Events Plug-in

- We now properly compare string values when processing alarms. Strings were previously compared as numeric values.

- Added enabled/disabled state icons to the list view used to configure sub-conditions. This allows users to know if the sub-conditions are either disabled or enabled. Users must also enable the additional sub-conditions they wish to use for multi-level conditions.

Advanced Tags Plug-in

- Added support for Link Tags.  This feature allows data to be transferred between two devices or bridge servers to integrate data from different systems.  The tag creation GUI now allows multiple tags to be created from the same instance of the tag editor.

- Fixed failure to reject reads on inactive tags (i.e., tags that are not started).

- Scaled tags in derived expressions are now handled properly. The device data type (rather than the engineering data type) was previously being used for expression evaluation. This would result in a failure to evaluate expressions even if the scaled data type was valid.

- LBCD and BCD data types are now allowed in derived expressions as they were in 4x. The server treats data from these types as DWORD and WORD, respectively.

- Added support for the F1 button to invoke the Advanced Tags help file when Advanced Tab is selected.

- Fixed a bug where a complex tag with no complex elements failed to load when saved in XML. We were not serializing the element list for this case, which is required by the schema.

- The complete tag for complex tags, complex elements, and derived tags is now optional.

- The tool tips for the Advanced Tag GUI buttons are now the same as the ones in the device view tag dialog. Support was also added for the Alt+L shortcut to open/close the select tag GUI.

- Advanced tags are now included in the project tag count (File | Project Properties | Identification).

- The GUI now enforces the fact that Complete Tags in Complex and Derived tags must be writeable.

- The scan rate for tags contained in Derived tags and Complex tags is now set to the trigger rate if the tag is triggering on a timer. This way the Complex/Derived tag will update at the trigger rate if the data is changing fast enough.

- Fixed issue with saving Advanced Tags in an XML project. We were failing to save the advanced tags in the root tag group.

Data Logger Plug-in

- Added unit selection (milliseconds, seconds, minutes, and hours) to "Update rate" control under the "General" tab, and to the "Static Interval" under the "Triggers" tab.

- Fixed issue where the rate was not being transformed into rate and resolution when loading from a legacy project.

- Set the default trigger interval from 100 to 500 milliseconds.

- Set the default Update Rate for triggers to 1000 milliseconds.

Oracle MES/MOC Connector

- Fixed issue with logging multiple tags in a complex update with MOC items.

- Logged data now records timestamps from when the data was received from the server and not when the data was forwarded and logged (as was previously the case).

- GUI updated with various enhancements

- Connection names can no longer have leading or trailing whitespace.

### Native Client Interfaces

Wonderware SuiteLink/FastDDE

- Added support for handling driver-supplied timestamp.

UA Server Interface

- Fixed incorrect deadband logic where we were updating the UA cached value regardless of whether the update passed deadband. This was causing a failure to update clients if the value incremented past the deadband limit.

- Fixed issue with loading certificate files from a certificate store (directory) that is identified with a string containing non-ASCII characters.

- Fixed issue where pending read or write transactions were not properly closed when the server shuts down.

- Prevent crash when attempting to run the server interactively from the Guest account.

OPC DA Server Interface

- Fixed an OPC DA 3.0 issue with the “IOPCBrowse” interface where the server was not returning the correct HRESULT if one or more of the item properties could not be retrieved.  The correct behavior is to return “S_FALSE” in this case instead of always returning the HRESULT from GetProperties() for the last leaf item in the browse item set.

- Fixed OPC compliance issue with reads in situations where the system clock is not monotonically increasing.

- Fixed failure to return device data following async read from device.  Problem is exposed when deadband is enabled on the item that is being read.

### Components / Utilities

UA Configuration Manager

- Fixed issue where an Instance Certificate could not be exported from the UA manager on some foreign language OSs.

- We now create the rejected or trusted store if they do not exist when trusting/rejecting a certificate.

- Added events and event logging support to the OPC UA Configuration Manager.

- Fixed issue when changing the enabled state of an endpoint and then attempting to accept some other edit made to it.

- Prevent duplicate names from appearing in the Discovery Server list.

- The GUI was updated to support viewing rejected certificates on the 'Trusted Clients' and 'Trusted Servers’ pages, with the option to trust them by right-clicking and selecting “Trust”.

OPC Quick Client

A checkbox was added to the Tools | Options dialog to ignore path elements containing a leading underscore when auto-building a project.

Drivers

Allen-Bradley ControlLogix Ethernet

- Added support for RSLogix version 18.

Allen-Bradley DF1

- Added an option in the driver called “Allow Float access to Micrologix/SLC N Files”.

Allen Bradley DHP

- Added .LEN field support for string files (PLC-5 only)

- Added .EN support for block transfer files

- Added status word access (.S field) to:

  - timer files

  - counter files

  - control files

  - block transfer files

- Added support for new SFC status file (SC)

- Added new syntax for ASCII files.

  - An:e maps to either a byte/char or a word data type, and contains two characters per element

  - An:e/b maps to either a string or a boolean data type

  - An:e[r][c] maps to either a char/byte or a word data type

  - An:e[c] maps to either a char/byte or a word data type

- Enabled boolean (/b) access for the word fields of the following structured files

  - timer			(.ACC, .PRE)

  - counter			(.ACC, .PRE)

  - control			(.POS, .LEN)

  - block transfer	             (.FILE, .ELEM)

  - PID			(.FILE, .ELEM)

- Enabled boolean (/b) access for BCD files

- Fixed issue where the element offset was not being set for Booleans. This caused Booleans which were not located in the first word of a structured file to be read and written to incorrectly.

DNP Master Serial

- Initial release of DNP drivers in 5x.

DNP Master Ethernet

- Initial release of DNP drivers in 5x.

GE Ethernet

- Fixed issue where PACSystem UDT discrete data types were not being read or written properly.

GE Focas Ethernet

- Fixed issue where all models except the Series 15i had one or more invalid address ranges.  The bug was introduced with the addition of CNC status info tags.

Hilscher Universal

- Fixed issue where the driver was not applying channel property changes when the Synchronize button was clicked. The result was that the tags being generated by the runtime could be out of sync with the server configuration.

Mitsubishi Ethernet

- Added support for "L" suffix to CN type.

- Fixed issue where address parser allowed Date data types for bit addresses.

- No longer deactivate tags for out of range errors.

- Enhanced Event Log messages for read and write errors.

- Added support for ZR file registers to the Q Series model.

BACnet

- Fixed issue where the driver did not ask for one of the object names listed in the device when requesting Auto Tag Generation one item at a time. This name is used when “Use Object Name for Tag Group Names” is selected under the “Tag Import” tab under “Device Properties”.

Beckhoff TwinCat

- Fixed issue where the driver was unable to load tags in structures from a tpy file for a BC/BX device.

Omron FINS Serial

- Fixed Address Hints for the C500 IR register.

- Added two new string types:

  - XXX as string with Only the Low Order byte (LSB - least significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenE

  - XXX as string with Only the High Order byte(MSB - most significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenD

Omron Fins Ethernet

- Fixed Address Hints for the C500 IR register.

- Added two new string types:

  - XXX as string with Only the Low Order byte (LSB - least significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenE

  - XXX as string with Only the High Order byte(MSB - most significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenD

Omron Host Link

- Added two new string types:

  - XXX as string with Only the Low Order byte (LSB - least significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenE

  - XXX as string with Only the High Order byte(MSB - most significant 8-bits) of each word is used for read/write. , Syntax: XXXaddr.lenD

ODBC

- Fixed issue where the time stamps from reads of Oracle 10g failed because the returned string includes microsecond resolution. We now truncate the string to place it in a known format.

SNMP

- The default SNMP MIB template selection was changed from "Switch" to "Other".

- Fixed bug where driver was using an invalid transaction id format, resulting in unnecessary transaction retries.

- Added support for auto device discovery.

Custom Interface Driver (CID)

- Fixed issue where it was possible to get into an infinite loop when multiple writes were made in rapid succession to the same tag.

OPC DA Client

- The driver now reports a value, quality, and timestamp for invalid tags (tags that cannot be added to the remote server). Previously we would keep attempting to read the tags, expecting an initial update. In the case that the tag is invalid, we will not receive an update, and should report the tag as “Bad: Out of Service”.

- The performance of Auto Tag Generation has been enhanced.

- The driver now removes all items from the underlying server when the DA Client’s device is configured as “disabled”.

- Fixed issue where the driver returned an invalid read value when an item did not receive an update from the DA Server. We now continue to process the read request until we have a valid return value.

OPC UA Client

- The driver now reports a value, quality, and timestamp for invalid tags (tags that can't be added to the remote server).  Previously we would keep attempting to read the tags, expecting an initial update (see KS-10563). In the case that the tag is invalid we won't receive an update, and should report the tag is BAD.

- Fixed issue where the requested data type was not being honored when providing tag updates on monitored items.

- Fixed bug where the password was not cleared in the decryption logic if the password was empty. This caused the runtime and the configuration to get out of sync with channel passwords.

- The performance of Auto Tag Generation has been enhanced.

- Fixed issue where we fail to connect to our own UA server if we are using a username/password and no security.

- The client driver now places the server certificate in the rejected store if it fails to connect with security. In the configuration we also display a message box that allows the user to trust an untrusted endpoint.

- Added synchronization and error checking for session read and write callbacks.

- The driver now removes all items from the underlying server when the UA Client’s device is configured as disabled.

- Fixed issue where the UA Client Driver returned an invalid read value when an item did not receive an update from the UA Server. We now continue to process the read request until we have a valid return value.

Ping

- Added support for Device Discovery.

Siemens TCP/IP Ethernet

- Added support for Siemens S7-1200 model.

SIXNET UDR

- Reference to SIXNET files 'six32com.exe' and 'udrcom32.dll' was changed from windows\system32 to the application’s root directory. This ensures that the driver will use its compatible version and not a version installed by other applications.

Torque Tool Ethernet

- A new setting was added under the Device Properties page to set the error state when a device fails to respond to writes or subscription requests.

User Configurable (UCON)

- Fixed issue where the “Invalidate Tag” command would not invalidate tags inside of a “Tag Block”.

- Added support for Custom #12 (8-bit) checksum. This is a variation on the Sum (8-bit) Check Sum. Input data is assumed to be in Ascii Hex.  Data is converted to hex before sum. The sum is then subtracted from 0xFF.

- Added model to support string based IDs. The model affects the formats available in the Write Device ID command and the Test Device ID command.

- ASCII Real and ASCII Real (packed 6 bit) format property pages have been modified to be more user-friendly.

- Fixed issue where Function Blocks and Global Buffer Preset were saved as part of an xml server project but were not available in the project when reloaded.

Yaskawa MP Ethernet

- Fixed writes to addresses MB04096-MB65534.

# TOP Server Release Note (5.2.133.0) February 18, 2010

### Administration Interface

- Added support for OPC UA Configuration management

- From the Settings | Configuration tab added ability to enable remote connections to support Exchange feature of UA Configuration Manager (secure by default).

### Configuration Interface

- Added support for OPC UA Project Configuration

- Fixed failure to close the channel diagnostics window attached to a recently deleted channel.

- Fixed "Runtime Update Failed" messages following tag duplication, object paste.

- Fixed the print button in the event log print preview.

- Resolved issue where the DCOM setting ‘Identity’ for the Configuration Client was not retained when "The launching user" option was selected.

- Updated project handling logic for case where a Read/Write user was not given a warning to save a modified project offline before loading new project.

- Updated project handling logic to prevent an update to the Runtime when connecting the Configuration as a Read Only user.

- Issue in the 5.1 release only, fixed failure to launch the server runtime process from the Configuration client if the Runtime is configured for interactive use and UAC is enabled.

- Updated the Alias browse GUI to eliminate the dependence on the parent dialog's check box with corresponding help update to better describe the “Show systems tag group:” checkbox.

- Added enable/disable checkbox for A&E project settings.

### Runtime Interface

- New OPC UA server interface V1.01 supporting optimized binary TCP.

- Improved DDE server capability when running as a service, to prevent MS Excel DDE client stability issues. (Requires interact with desktop to be enabled.)

- Fixed failure to apply Alias scan rate override to items added via the FastDDE/SuiteLink native interface.

- Added the ability for a user to specify the 'default' project to use the next time the runtime is started. The Runtime will look for user-supplied project.xml or project.opf file in the same directory as the default.opf at server startup and reinitialize.

- Fixed problem were no client update was being generated from the OPC layer upon item state transition from inactive to active.

### Event Log

- None

### Components / Utilities

OPC UA Configuration Manager

- New utility which always installs due to install of OPC UA server interface.

OPC A&E Server

- Fixed a COM error when the server forced client deletion. The error resulted in stability issues with the runtime.

License Utility

- Several minor cosmetic updates to the UI.

- Added the following warning text to the software activations page:  “Caution: Multiple licenses of the same product cannot be activated on one machine. Attempting to do so will result in the loss of the license.”

OPC Quick Client

- Enhanced the Quick Client to better support international value formats where a comma is used instead of a decimal point for floating point numbers.

### Install

- Add the ability for the user to override the default root for application data. This enhancement is for users of systems (i.e. embedded OS) where a “SharedApplicationDataDirectory” may not have write privileges or may not exist. When performing un-installs, the product.ini file will not be deleted.

- Fixed issue found internally where a Windows SxS error is recorded in the application event log during product installation.

- Enhanced digital signature verification logic to no longer depend on CAPICOM (which is deprecated in Windows 7). Removed CAPICOM from install.

- Resolved issue with 5.1 install where an upgrade from 5.0 to 5.1 caused the process mode to change from Interactive to Service.

- Make installing the A&E Custom Alarms Plug-in optional, but give all users the OPC A&E server interface (event log messages to A&E clients) by default.

- Updated hardware key drivers (HASP SRM command line installation) to support Windows 7. Tested with 32/64 bit operating systems.

- Replaced old SimDemo.opf sample project with a more modern sample.

- Install on Windows 2000 will prompt user to reboot and restart install after VS2005 installed.

### Plug-ins

A&E Custom Alarms

- New licensed plug-in.

DataLogger Plug-In

- Fixed issue where deadlock could occur after starting/stopping a log group.

- Fixed an issue where table creation with Oracle databases was not working.

Drivers

All Drivers

- Improved device read queue logic to prevent potential deadlock scenario. This issue was found during internally testing.

Allen-Bradley ControlLogix Ethernet

- Modified the driver to support locale-specific multi-byte strings.

- Resolved an issue with Auto Tag Generation that occurred if a project correlation error was detected.

- Increased the maximum number of Programs supported from 512 to 1024.

- Fixed application exception that can occur when multiple Logix Array elements are added and removed at random, followed up by a project upload (due to inactivity, change in project, etc).

BACnet

- Modified driver to not repeatedly request the "Segmentation Supported" property from a device if the device returns an error to that request.

- Fixed ATDBG when the device responds with an error to the Read Property: ALL command.

- Corrected a problem with parsing a NotificationClass Object.  This was causing ATDBG to fail with an internal test device, and generating default tags.

- Resolved issue with permanent COV subscriptions.

- Enhanced COV Subscription Request handling to improve performance

Cutler-Hammer ELC Ethernet

- Fixed issue with write-only tags introduced in 5.0.  The value of the tag was not updating when a value was written to it.  The correct value was written to the device, just not displayed in the data client.

Cutler-Hammer ELC Serial

- Fixed issue with write-only tags introduced in 5.0.  The value of the tag was not updating when a value was written to it.  The correct value was written to the device, just not displayed in the data client.

Dataforth IsoLynx

- Fixed issue introduced in 5x where reconnect to device after a cable pull can take minutes instead of seconds as in V4.x version of driver.

GE Ethernet

- Fixed issue where PACSystem UDT booleans were not being read or written properly

GE Focas1 Ethernet

- Fixed address parser problem introduced with addition of CNC status info tags.

Honeywell HC900 Ethernet

- Replaced broken "Regenerate imported tags" checkbox with a regenerate button.  The regenerate button gives the same intended functionality as the "Regenerate imported tags" checkbox.

- Fixed issue where the driver did not support proper importation of certain digital addresses such as digital floats.

Idec Serial

- Expand the address ranges as for MicroSmart and Open models.

- Added support for Floats to Data Registers for MicroSmart, Micro3, and Open models.

Mettler Toledo Serial

- Added write-only Booleans CTPZ commands (Clear, Tare, Print, Zero).

- Enabled Unsolicited Ethernet Encapsulation.

Modbus Ethernet

- Fixed issue with write-only tags introduced in 5.0.  The value of the tag was not updating when a value was written to it.  The correct value was written to the device, just not displayed in the data client.

- Allow global settings that control unsolicited port and protocol to change on the fly.

Modbus Serial

- Fixed issue with write-only tags introduced in 5.0.  The value of the tag was not updating when a value was written to it.  The correct value was written to the device, just not displayed in the data client.

Omron FINS Ethernet

- Fixed thread synchronization issue which could result in intermittent stale communications for certain channels in multi-channel projects

OPC UA Client Driver

- new driver

Opto 22 Ethernet

- Fixed issue with processing "Object not found" Errors when using "CONT over Ethernet TCP/IP" Communications Protocol.

SattBus Serial

- Resolved issue where the driver was not removing tag(s) from its tag table when the client application disconnects.

Siemens TCPIP Ethernet

- Fixed issue where the Runtime could terminate after multiple writes to bit addresses.

- Resolved issue introduced in 5.1 release where device-level _System tags (_Error,_NoError) were not working properly.

Sixnet UDR Serial

- Fixed access violation when the driver dll is unloaded and reloaded.

SNMP

- Fixed Trap event handler to receive Traps correctly after IP changes when the device is in use (has active items).

- Disabled Scan Floor and Lock controls on Device Communications property page if the device is in use (has active items).

U-CON

- Added ability to select any character as the escape character for a selected group of control characters to the Handle Escape Character command.

- Fixed issue where format properties for commands were not preserved in the transaction editor on loading a command's properties.

# TOP Server Release Notes (5.1.71.0) October 21, 2009

### Server updates

- Runtime now detects install event and preserves DCOM configuration if present on an upgrade installation.

- Fixed anomaly where channel diagnostics no longer work following a name change to a channel.

- Added plug-in client counts to the server’s data client count _AEClinetCount

- Fixed anomaly where alias references specified as <alias>.<tag group>.<tag name> were not getting resolved.

- Fixed anomaly where server fails to auto-generate a system alias when a tag group is added from the configuration client and the parent of that tag group is an internal tag group managed by a plug-in.

- Fixed anomaly where the alias map was not being updated following a channel/device rename in offline mode.

- Fixed anomaly with the Alias Name dialog where the dialog would not allow an alias to be created that maps to a channel.

- Added event log notification “Channel diagnostics started/stopped on channel '<channel name>' to the event log.

- "Demo timer started" event log message now shows the feature name that tripped the demo timer and the basic condition for the timer: i.e. not licensed, limited license or license limits exceeded.

- Fixed anomaly when tag is duplicated using the "Duplicate" button on the tag dialog and has address longer than 512 chars.

- Tag addresses that contain a leading zero now get incremented when using the duplicate button on the tag dialog.

- Fixed anomaly where user would get a "Runtime update failed" message box when attempting to add more channels than allowed by the driver

- Increased tag address limit to 1024 chars to agree with legacy v4 server.

- Alias names are now auto generated for system and plug-in tags.

- We now preserve server options of legacy v4 projects on project load.

- Fixed anomaly where the modem tab on the channel property page was not being shown on initial startup of the configuration utility after the modem had been installed.

- Fixed anomaly where the TAPI layer was not functioning properly when running as a service, thus affecting proper modem functionality.

- Fixed an anomaly where the event log entries were not getting preserved in the eventlogserver_eventlog.log file after a clean install.

### Components / Utilities

License Activation Utility

- Removed the “Transfer License Response" option from License Utility because it is no longer necessary for a user to process a transfer response file.

- Fixed anomaly where the font size was incorrect on Chinese OS.

### Driver Enhancements/Fixes

Advanced Tags

- Fixed anomaly with the Derived Tag update rate where the update was being executed every timer tick (100msec), instead of respecting the specified tag update rate.

Alarm & Events Plug-in (New)

- Supports OPC Alarms & Events for Event Log messages

DataLogger Plug-in

- Fixed an anomaly where the 'Server Item Parameters' column in the 'Map Item Fields' dialog was being incorrectly populated for wide log groups. This occurred only when loading a project in OPF format.

- Added a DataLogger transform for proper conversion of XML projects from 4x.

- Fixed an anomaly where NULL values were written to the database when logging in wide format with an on data change trigger. Previously only values that changed were written to the database. Stale values were written as NULL. This behavior does not match 4x. Now cached values are written to the database for values that have not changed.

- Fixed anomaly where the user was inadvertently allowed to enter text into the log item dialog's 'DataType' combo box.

- Fixed anomaly where the log group _Error tag was not going to a true state when the log group’s DSN is invalid.

- Fixed anomaly where user could not pick proper regional time formatting for data/time in the Absolute Trigger dialog.

Automation Direct Productivity 3000 (New)

Custom Interface (New)

Mettler Toledo (New)

Allen-Bradley DH+

- Fixed inconsistencies for each configured card type when there is actually no card present.

Allen-Bradley ControlLogix

- Fixed anomaly where L5K files with lines longer than 32768 characters would not import correctly.

- Added support for automatic tag database generation using .L5X files.

- Fixed Predefined Data Type tag names created during an L5K/L5X import to match the new names used in online tag generation with V17.

- Added support for asynchronous hostname resolution.

- Added support for predefined types as part of support for firmware revision 17.

Allen-Bradley Unsolicited Ethernet

- Fixed anomaly where word order was being swapped on 32 Bit data types.  Added a device prop to disable word swapping: "first word low".

GE Ethernet Global Data

- Added event log information displaying the channel to which the consumer or producer belongs to when binding a Producer Socket to the Default Network Adapter.

GE Ethernet

- Fixed anomaly where symbolic Float and Double tags were showing 1.#INF (invalid Float) instead of “0” value.

- Now allow for the alias tag data types that are specified as BOOL to assume the source tag data type.

- Fixed anomaly where address parsing of non-register, non-string memory types allowed a "-" in the address field.

- Added support for DOUBLE data types.

GE Focas 1

- Added support for CNC Status Info tags.

GESNP

- Now allow for the alias tag data types that are specified as BOOL to assume the source tag data type.

- Fixed anomaly where address parsing of non-register, non-string memory types allowed a "-" in the address field.

GESNPX

- Now allow for the alias tag data types that are specified as BOOL to assume the source tag data type.

- Fixed anomaly where address parsing of non-register, non-string memory types allowed a "-" in the address field.

Mitsibushi A Ethernet

- Added support for Double and Date data types to A Series and FX3U models.

- Added support for Extended Data Registers to Q series models.

- Added support for Extended Link Registers to Q series models.

- Added support for Double and Date data types to Q series models.

Modbus ASCII

- Added string data type support for Internal Registers.

Modbus Ethernet

- Added string data type support for Internal Registers.

Modbus Plus

- Added string data type support for Internal Registers.

- Added block string read support.

Modbus RTU

- Added string data type support for Internal Registers.

- Added block string read support.

Modbus RTU Unsolicited

- Added string data type support for Internal Registers.

Siemens S7 MPI

- Fixed anomaly creating tags defined with String data type.

Siemens S5 (3964R protocol)

- Fixed how KC memory types are displayed.  Counters are now limited to three BCD nibbles for KC; this reflects how the data is stored on the physical device.

- Fixed anomaly where arrays for Counter Current values C and Z were accepting out of range values.

Siemens TCP/IP Ethernet

- Added support for DNS hostname resolution.

- Fixed anomaly where driver was posting multiple “Device Not Responding” messages.

Simatic 505 Ethernet

- Fixed anomaly where driver was unable to communicate to certain devices that emulate a 505 Series PLC/NITP protocol and do not support 32bit addresses in command.

SNMP

- Added auto tag generation support for a variation of a “trap OID” containing an enterprise specific type. This format comes in as an instance of (.0) an OID with the last sub ID identifying the enterprise specific type (e.g., 1.3.6.1.4.1.318.0.12). We are required to create a tag with an address that contains the enterprise specific type (e.g., TRAP_V1:.1.3.6.1.4.1.318:G6:S12)

Triconex Ethernet

- Fixed anomaly where the driver failed to import a mixture of both name aliases and Modbus aliases.

User Configurable (UCON)

- Fixed anomaly where Transmit Byte command and Clear Rolling Buffer command were allowed to be selected from the menu without selecting a transaction in the item view.

Yokogawa DX Ethernet

- Fixed anomaly with log scaled channels on a DX2020. The DX "advanced" model used different scale factors for channel data than the standard DX models.

# TOP Server Release Notes (5.0.1176) July 22, 2009

### TOP Server Version 5 is a major upgrade that adds new functionality, support for the latest Windows operating systems, and provides an architecture through which you’ll receive many new features over the coming years.

### The full release notes for Version 5.0.1176.0 for any drivers match the last Release Notes for version 4 and can be found below.

### More details on Version 5 can be found here.

### Driver Enhancements/Fixes

BACnet Driver

- Fixed channel wizard issue that prevented user from moving to next page, incorrectly indicating that another channel was configured with same NIC and port.

- Fixed an issue with processing “read property multiple” responses from certain brands of hardware, which resulted in toggling quality of all items associated with an object and repeated “device not responding” errors.

Beckhoff Driver

- Fixed anomaly where writes to IO could fail, and reads from IO would not always report the correct values.

ControlLogix Ethernet Driver

- Fixed performance issue for DH+ Gateway, ControlNet Gateway, ENI and Micrologix models where writes and priority reads could be starved in a low bandwidth/slow response time scenario.

- Fixed issue where the driver generated names for imported array tags with 'CONDENSED' tag hierarchy incorrectly.  The generated names were instead in the EXPANDED format.

- Fixed L5K auto tag generation issue where L5K ENCODED_DATA and FBD_ROUTINE blocks were not being properly ignored.

- Fixed issue where the driver could occasionally read/write empty data for string tags. This only happens for projects with multiple channels.

UCON Driver

- Fixed issue where the Event counter was not incrementing for unsolicited transactions when a command preceded the initial read response.

- Fixed issue with ASCII Real and ASCII Real (packed 6-bit) formats where legacy projects failed to load a default value for the "Use decimal comma in place of decimal point" option in the format properties.  This resulted in projects behaving as though it was set even though the check box was not marked.  Viewing the dialog box would set the property to the default value (unchecked/false).

- Fixed issue with ASCII Real and ASCII Real (packed 6-bit) formats where non-negative numbers with negative exponents only displayed the exponent.

Idec Driver

- Added support for "Extra Data Register" (D10000-D49999) for the MicroSmart model. For MicroSmart  modules (non Slim Type CPU modules) that do not support the "Extra Data Registers" the driver will report a failure when reading/writing these registers.

SquareD Driver

- Fixed issue where the driver was not parsing received data packet correctly when the route ID contained one or more nodes that were not equal to 255.

Yokogawa CX Ethernet

- Fixed issue where would inefficiently time out on the device if the device returned an error code, rather than processing the error and immediately moving on to the next request