VM5

PSTN/GSM INTERFACE

Technical Documentation

HW version - V1.1

TABLE OF CONTENTS

1 INTRODUCTION	5

2 CONNECTION	6

3 THE VM5 PCB AND BLOCK TERMINALS	7

4 DISCRIPTIONS OF TERMINAL BLOCKS 	8

4.1 TLb – PSTN standard telephone - line b	8

5 VM5 - PROGRAMMING MODE	10

6 INDICATIONS	12

7 USING THE VM5 LIKE PSTN/GSM INTERFACE WITH ADDITIONAL ALARM INPUTS AND OUTPUTS	13

7.1 HOW TO PROGRAM TELEPHONE NUMBERS	13

7.1.1 Programming table – direct programming on SIM	13

7.1.2 TL remote programming by SMS	14

7.2 HOW TO PROGRAM INPUT STATUS 	14

7.2.1 Typical input connections	14

7.2.2 Programming table for input status	15

7.2.3 IP remote programming by SMS	15

7.3 HOW TO PROGRAM OUTPUT STATUS 	15

7.3.1 Typical connection of the output	16

7.3.2 Programming table for output status	16

7.3.3 OP remote programming by SMS	17

7.4 DIRECT ALARM OUTPUT – OA	17

7.4.1 Programming table for OA – direct alarm output	17

7.4.2 OA remote programming by SMS	18

7.5 INPUTS AND TELEPHONE NUMBERS LINKING	18

7.5.1 Programming table for linking the inputs and telephone numbers	18

7.5.2 LK remote programming by SMS	19

7.6 INPUT DELAY BEFORE DIALLING	19

7.6.1 Programming table to define the delay before dialing procedure	19

7.6.2 DL parameter remote programming by SMS	20

7.7 INPUT FILTER PARAMETR  	20

7.7.1 Programming table to define the value of the input filter	20

7.7.2 IF parameter remote programming by SMS	21

7.8 CLIP TELEPHONE NUMBERS – TO	21

7.8.1 Programming table to define the clip telephone numbers – TO	21

7.8.2 TO parameter remote programming by SMS	22

7.9 SECURITY TELEPHONE NUMBERS - TK	22

7.9.1 TK PARAMETER REMOTE PROGRAMMING BY SMS	23

7.10 PRE-PAY CARD CREDIT AND VALIDITY INFORMATION	23

7.10.1 Programming pre pay card credit and validity string	24

7.10.2 V parameter remote programming	24

7.11 VM5 – GSM SET-UP PARAMERTERS 	24

7.11.1 PROGRAMMING TABLE FOR VM5 – GSM SET-UP PARAMERTERS	25

7.11.2 Set-up parameters programming by SMS	26

7.12 SMS MESSAGES ORGANISER	26

7.12.1 SMS MESSAGES PROGRAMMING TABLE	26

8 VM5 SMS REMOTE COMMANDS	28

8.1 PRINT-OUT OF THE PARAMETERS	28

8.1.1 Receive all parameters (PRALL) 	28

8.1.2 Receive telephone numbers (PRTL)	28

8.1.3 Receive links (PRLK)	28

8.1.4 Receive input parameters (PRIP)	28

8.1.5 Receive input filter value (PRIF)	28

8.1.6 Receive clip identification telephone numbers (PRTO)	28

8.1.7 Receive access telephone numbers (PRTK)	29

8.1.8 Receive output parameters (PROP)	29

8.1.9 Receive link for local alarm output (PROA)	29

8.1.10 Receive delay before dial (PRDL)	29

8.1.11 Receive all programmed SMS messages (PR#)	29

8.1.12 Receive set up parameters value (PRP)	29

8.1.13 State of the credit for the pre-pay card	30

9 CHECKING AND CHANGING THE SYSTEM STATUS (ON/OFF)	31

9.1.1 Checking system status by SMS command	31

9.1.2 Changing system status off to on (system on)	31

9.1.3 Changing system status ON to OFF (system OFF)	31

10 CHECKING THE INPUT STATUS	32

10.1 CHECKING THE INPUT STATUS BY SMS (INP)	32

11 OUTPUTS REMOTE CONTROL 	33

11.1 OUTPUTS REMOTE CINTROL BY SMS COMMAND	33

12 CLEAR ALL PROGRAMMED DATA FROM SIM	34

13 HOW TO CHANGE PARAMETERS USING THE SMS COMMAND	35

14 START UP	37

15 APPENDIX A - ADDITIONAL VM5 FEATURES	38

15.1 “MAIN POWER LOST” and telephone numbers linking - LK6, LK7	38

15.1.1 Programming table for “MAIN POWER LOST” and telephone numbers linking	38

15.1.2 LK remote programming by SMS	38

15.2 “LOW BATTERY” AND TELEPHONE NUMBERS LINKING – LK7, LK8	39

15.2.1 Programming table for “LOW BATTERY” and telephone numbers linking	39

15.2.2 LK6 and LK7 remote programming by SMS	39

15.3 “MAIN POWER LOST” FILTER PARAMETR - VMT  	39

15.3.1 Programming table for “MAIN POWER LOST” filter – VMT	40

15.3.2 “MAIN POWER LOST” filter remote programming by SMS	40

15.4 “LOW BATTERY” filter parameter - VBT 	40

15.4.1 Programming table for “LOW BATTERY” filter - VBT	40

15.4.2 “LOW BATTERY” filter remote programming by SMS	41

15.5 “MAIN POWER LOST” and “LOW BATTERY” TEXT EDITOR 	41

15.5.1 Programming table for “MAIN POWER LOST” and “LOW BATTERY” text messages	41

15.5.2 “MAIN POWER LOST“ and “LOW BATTERY” text messages remote programming by SMS	41

15.6 INPUT TRIGGER COUNTER BEFORE ALARM - IC 	42

15.6.1 Programming table for the input trigger counter - IC	42

15.6.2 The input trigger counter before alarm remote programming by SMS	42

15.7 INPUT TRIGGER COUNT UP INACTIVITY PRESET – IR	42

15.7.1 Programming table for the input trigger count up inactivity preset - IR	43

15.7.2 The input trigger count up inactivity preset remote programming by SMS	43

15.8 ACTIV ALARM SMS MESSAGE RE-SEND TIME - IA	43

15.8.1 Programming table for the activ alarm re-send time - IA	44

15.8.2 The activ alarm re-send time remote programming by SMS	44

16 TECHNICAL DATA	45

16.1 Gsm main features	45

17 VM5 typical connections	46

# INTRODUCTION

NOTE:

The basic functions on the VM5 are exactly the same like on the VM3. VM5 has additional Inputs and Outputs and programming of them is the same like with GSM-VAC+. The default values (diagnostic) of I/O are the same like VM3 had.

VM5 can be use for different applications in GSM network:

- Back-Up for standard PSTN telephone line

- Standalone telecommunication unit (instead off PSTN line)

- Money saver in offices; GSM to GSM  calls from desk phone (FCT- Fixed Cellular Terminal )

VM5 can also be used in connection with different telephone equipment such a:

- Alarm panels with built in digital communicator

- Automatic voice, digital or signal telephone dialers

- Standard telephone sets

- PABX – private telephone exchanges

NOTE:

VM5 is an interface between analog telephone equipment and    GSM network. It aloud to transmit exactly the same data which are programmed in Alarm Control Panel or other communication device (for instance: ID protocol, Voice messages...). It can also be used for voice communication between two users.

# CONNECTION

Insert SIM card into your personal GSM phone and program the parameters you need (see chap. PROGRAMING).

Insert SIM card into SIM holder on GSM module.

Connect Power Supply – (12 – 16V DC). Use the power from the Alarm Control Panel or wall adapter power supply.

Connect the Back-up battery – (12V/0.8 Ah).

Connect the standard PSTN telephone line – (if present) on terminal blocks TLa1/TLb1.

Connect a telephone unit – (Control panel, telephone dialer, telephone set…) on terminal blocks Ta1/Tb1.

# THE VM5 PCB AND BLOCK TERMINALS

# DISCRIPTIONS OF TERMINAL BLOCKS

ACCU/GND - Battery back up connector. In the original metal box it’s possible to place a 0.8Ah/12V battery.  Red fasten connector is for positive and black fasten connector is for negative voltage battery supply.

+12V/GND - Power Supply connector; on the left side is positive voltage (+ 12 VDC) and the right site is GND voltage.

Ta1/Tb2 - Terminal blocks for telephone connecting on the VM5 artificial telephone line. When the PSTN line is connected on the VM5 (Tla/Tlb) all communication will be carry out thought PSTN line. If telephone line is cut off, VM5 will automatically switch on the artificial telephone line and the communication will be carry out by GSM network. In case if standard telephone line is not present at all, it will work automatically thought GSM network.

Ta1 – (TIP)

Tb1 – (RING)

TLa/TLb - Terminal blocks for standard telephone line connecting. It is possible to connect telephone line from public telephone network (PSTN) or internal telephone line from office telephone exchange (PABX).

TLa – PSTN standard telephone - line a

## TLb – PSTN standard telephone - line b

GND - solid earth ground

TAMP/TAMP - Terminal blocks for connecting anti-tamper loop from tamper switches (upper and bottom) on PCB (N.C.).

IN1 – Alarm input 1. It can be N.O. (normal open) to GND or +12V DC, N.C. (normal close) to GND or +12V DC. Default is N.O. to GND.

IN2 – Alarm input 2. It can be N.O. (normal open) to GND or +12V DC, N.C. (normal close) to GND or +12V DC. Default is N.O. to GND.

IN3 – Alarm input 3. It can be N.O. (normal open) to GND or +12V DC, N.C. (normal close) to GND or +12V DC. Default is N.O. to GND.

IN4 – Alarm input 4. It can be N.O. (normal open) to GND or +12V DC, N.C. (normal close) to GND or +12V DC. Default is N.O. to GND.

NOTE:

By default the Input 4 has “GSM NETWORK PRIORITY” function. When you put the right potential on the IN4 (look the IP parameters) the VM5 will automatically switch to the GSM network even if the PSTN line is present.

OUT1 – First diagnostic, remote control or alarm output. It is Open Collector output with maximum loading current of 220mA. By default this output is diagnostic for the PSTN line trouble.

OUT2 – Second diagnostic, remote control or alarm output. It is Open Collector output with maximum loading current of 220mA. By default this output is diagnostic for the GSM network trouble.

OUT3 – Third diagnostic, remote control or alarm output. It is Open Collector output with maximum loading current of 220mA. By default this output is diagnostic for the low level of the GSM signal.

OUT4 – Fourth diagnostic, remote control or alarm output. It is Open Collector output with maximum loading current of 220mA. By default this output is not use for diagnostic and it can be use like a remote control or alarm output.

# VM5 - PROGRAMMING MODE

IMPORTANT!!!

Before you insert the SIM card into holder of GSM module or external GSM phone, please disable the PIN CODE!!!!

To program the VM5 parameters put the SIM card into your personal GSM phone. Add programming parameters in SIM Card “Phone Book”.

You can program the VM5 also remotely by SMS command

For the basic functionality of the VM5 you can program following parameters:

- LANET – standard telephone line (PSTN) local area prefix (max. 4 No.)

- TLCHK – PSTN line check period (in seconds from 1 – 250)

- IDCON – ID CONTACT format (1 = ON, 0 = OFF)

- OUTPR – Exit number from PABX (office exchange, usually 0 or 9)

- GSMPR – GSM network priority – Input 4

SIM CARD PHONE BOOK

| Name | Number | Default | Comment |
| --- | --- | --- | --- |
| LANET | empty |  |  |
| TLCHK* | empty | 5 sec. | PSTN line check every 10 sec. |
| IDCON | empty or »0« |  | Normal Voice Channel |
| GSMPR | empty |  |  |
| OUTPR | empty |  |  |

NOTE:

When you use new or empty SIM card or any parameters weren’t programmed by you, VM5 will automatically accept the default values (see table).

How to program the parameters (example)

The local telephone number prefix for Bologna is 051.

The VM5 is connected on the local telephone exchange and outgoing number is »0«.

We'd like to check PSTN line every 30 second.

If the Input 4 goes active we want to switch on GSM network (even if the PSTN line is O.K.) after 15 seconds.

The protocol which we'd like to send to the Monitoring Station is ID contact. (See table)

SIM CARD PHONE BOOK

| NAME | NUMBER | Comment |
| --- | --- | --- |
| LANET | 051 | Local area prefix |
| TLCHK | 30 | PSTN line check every 30 sec. |
| IDCON | 1 | ID contact protocol |
| GSMPR | 15 | GSM network after 15 s - IN4 default |
| OUTPR | 0 | Outgoing prefix from PABX |

NOTE: If the value of the TLCHK is 0 then telephone line checking is disabling!

All this parameter you can also program remotely using the SMS command.

For example, for the upper case the SMS command is:

;LANET=051;TLCHK=30;IDCON=1;GSMPR=15;OUTPR=0;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+LANET=051;TLCHK=30;IDCON=1;GSMPR=15;OUTPR=0;

# INDICATIONS

VM5 use three LED diodes for status indication:

- LED 1 – blue

Indicate the level of GSM signal. LED flashes from 1 pulse (very bad signal) up to 5 pulses (very good signal).

- LED 2 – green

The LED 2 indicates when the unit is ON or OFF state. When the LED is ON also the unit is ON and alarm inputs are active. When the LED is OFF the alarm inputs are not active.

- LED 3 – red

The LED 3 is turned ON when a PSTN line is off (not connected or cut). When the red LED is »ON« the VM5 automatically uses GSM network for transmitting.

# USING THE VM5 LIKE PSTN/GSM INTERFACE WITH ADDITIONAL ALARM INPUTS AND OUTPUTS

The VM5 has full PSTN/GSM interface (VM3) functionality and it has also almost all features of a GSM alarm communicator with 4 alarm inputs and 4 remote control/alarm outputs. You can program Inputs and Outputs on the same way like the GSM-VAC+ unit.

## HOW TO PROGRAM TELEPHONE NUMBERS

### Programming table – direct programming on SIM

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Phone Number | Description |
| TL1 |  | 1st telephone number |
| TL1 |  | 2nd telephone number |
| TL2 |  | 3rd telephone number |
| TL3 |  | 4th telephone number |
| TL4 |  | 5th telephone number |
| TL5 |  | 6th telephone number |
| TL6 |  | 7th telephone number |
| TL7 |  | 8th telephone number |
| TL8 |  | 9th telephone number |
| TL9 |  | 10th telephone number |

VM5 – GSM can send only the DTMF alarm sound (not a voice message), a 14 character–SMS message or both. If the corresponding name ends with the letter “C”, only an alarm sound voice will be send; and if the name ends with the letter “S”, only the SMS will be send.

By pressing the * we switch off the redial call for calling number. The remaining numbers will be called as usual.

By pressing the # we switch off all remaining calls.

Example: We wish to send a voice and an SMS message to the first telephone number, only a voice message to the second one and only an SMS message to the third one. (See the table below.)

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Phone Number | Description |
| TL0 | 042364800 | 1st telephone number (voice & SMS message) |
| TL1C | 040713470 | 2nd telephone number (voice message only) |
| TL2S | 040307395 | 3rd telephone number (SMS message only) |

### TL remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;TL0=0402364800;TL1C=040713470;TL2S=040307395;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+TL0=0402364800;TL1C=040713470;TL2S=040307395;

## HOW TO PROGRAM INPUT STATUS

Alarm and reset input can be triggered in 4 different ways. The status of the input can either be normal closed (N.C) or normal open (N.O.) with positive (+ 12V) or negative (GND) voltage.

When you need the input feed back information it is possible to get SMS back when input will return from alarm to normal position. (See cap.7.8 – SMS Messages organizer). To get return SMS use IP=4,5 or 6.

- IPx = 0 – Normal Open – triggered with negative voltage (GND)

- IPx = 1 – Normal Close – breaking negative or positive voltage loop

- IPx = 2 – Normal Open – triggered with positive voltage (+ 12VDC)

- IPx = 3 – Input disable

- IPx = 4 = IP = 0 + input reset SMS

- IPx = 5 = IP = 1 + input reset SMS

- IPx = 6 = IP = 2 + input reset SMS

Note:

For reset SMS use message #6 for Input 1, #7 for Input 2, #8 for input 3 and #9 for input 4

### Typical input connections

### Programming table for input status

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IP0 | 0 | Input status for system ON/OFF |
| IP1 | 0 | Input status for alarm input 1 |
| IP2 | 0 | Input status for alarm input 2 |
| IP3 | 0 | Input status for alarm input 3 |
| IP4 | 0 | Input status for alarm input 4 |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| IP0 | 0 | OFF – when connecting GND on RST input |
| IP1 | 0 | Alarm activated by connecting to GND |
| IP2 | 1 | Alarm activated by disconnecting GND or +12V |
| IP3 | 2 | Alarm activated by connecting +12V |
| IP4 | 4 | Alarm activated by connecting to GND + RST SMS #6 |

### IP remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;IP0=0;IP1=0;IP2=1;IP3=2;IP4=4;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+IP0=0;IP1=0;IP2=1;IP3=2;IP4=4;

## HOW TO PROGRAM OUTPUT STATUS

The VM5 – GSM device has four open collector outputs and each of them can be programmed through network in a different way: as a bi-stable or mono-stable output. Any of them can be programmed also to signal certain failure on the main device or to notify us about the expiring validity of the SIM card.

### Typical connection of the output

### Programming table for output status

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| OP1 | 245 | Default for PSTN line failure |
| OP2 | 241 | Default for GSM network failure |
| OP3 | 247 | Default for low GSM signal antenna |
| OP4 | 243 | Default refill report |

OP (x) = 1 bi-stable ON/OFF mode

OP (x) = 2 – 240 mono-stable (pulse length in seconds)

OP (x) = 241 – GSM network failure default on the Output 2(H/L)

OP (x) = 242 – GSM network failure default on the Output 2 (L/H)

OP (x) = 243 – warning notice on the expiring validity of the SIM card (H/L)

OP (x) = 244 – warning notice on the expiring validity of the SIM card (L/H)

OP (x) = 245 – PSTN line failure (default on the Output 1) (H/L)

OP (x) = 246 – PSTN line failure (default on the Output 1) (L/H)

OP (x) = 247 – low GSM signal antenna default on the Output 3(H/L)

OP (x) = 248 – low GSM signal antenna default on the Output 3(L/H)

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| OP1 | 1 | ON/OFF mode output |
| OP2 | 245 | PSTN line failure |
| OP3 | 20 | 20 second pulse output |
| OP4 | 241 | GSM network trouble output |

### OP remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;OP1=1;OP2=245;OP3=20;OP4=241;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+OP1=1;OP2=245;OP3=20;OP4=241;

## DIRECT ALARM OUTPUT – OA

If you want to activate a local alarm (siren) you can program any VM5 output for this function.

Type of the Output (ON/OFF or pulse time) is determinate with parameter OP.

In the same time you can control the outputs also remotely.

Default value of OA parameters is:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number Default | Description |
| OA1 | 9 | No link between INx and OUTx |
| OA2 | 9 | No link between INx and OUTx |
| OA3 | 9 | No link between INx and OUTx |
| OA4 | 240 | Input 4 will force the VM5 on GSM network |

Possible programming parameters:

| Value | Description |
| --- | --- |
| 9 | Input used as normal alarm input |
| 10 | Output 1 OFF |
| 11 | Output 1 ON |
| 12 | Check Output 1 status (1 beeps – ON, 3 beeps – OFF) |
| 20 | Output 2 OFF |
| 21 | Output 2 ON |
| 22 | Check Output 2 status (1 beep – ON, 3 beeps – OFF) |
| 30 | Output 3 OFF |
| 31 | Output 3 ON |
| 32 | Check Output 3 status (1 beep – ON, 3 beeps – OFF) |
| 40 | Output 4 OFF |
| 41 | Output 4 ON |
| 42 | Check Output 4 status (1 beep – ON, 3 beeps – OFF) |
| 240 | GSM priority – VM5 forced to work on GSM network |

### Programming table for OA – direct alarm output

Example:

Input 1 (IN1) and Input2 (IN2) will activate the first Output (OUT1), Input 3 (IN3) will activate the second Output (OUT2) and Input 4 (IN4) will activate the third output (OUT3).

It is possible to choose different combinations between outputs and inputs

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number* | Description |
| OA1 | 240 | Input 1 will force the VM5 on GSM network |
| OA2 | 11 | Input 2 will trigger the Output 1 |
| OA3 | 21 | Input 3will trigger the Output 2 |
| OA4 | 31 | Input 4will trigger the Output 3 |

*NOTE: The first digit is output number and the second must be always 1

### OA remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;OA1=240;OA2=11;OA3=21;OA4=31;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ OA1=240;OA2=11;OA3=21;OA4=31;

## INPUTS AND TELEPHONE NUMBERS LINKING

It is possible to link each number or any combination of numbers to any of the four corresponding inputs. The link LK0 is specially designed for SIM card refill SMS warning message.

### Programming table for linking the inputs and telephone numbers

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| LK0 |  | Refill SIM – SMS (#0) & telephone No. link (TL0 - TL9) |
| LK1 |  | Input & telephone No. link for 1st alarm input (TL0 - TL9) |
| LK2 |  | Input & telephone No. link for 2nd alarm input (TL0 - TL9) |
| LK3 |  | Input & telephone No. link for 3rd alarm input (TL0 - TL9) |
| LK4 |  | Input & telephone No. link for 4th alarm input (TL0 - TL9) |
| LK5 |  | Test SMS and telephone No. link – SMS (#5) (TL0 - TL9) |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| LK0 | 01 | Refill SIM – SMS (#0) will be send to TL0 & TL1 |
| LK1 | 02 | Input1 will call/send SMS to TL0 & TL2 |
| LK2 | 023 | Input2 will call/send SMS to TL0, TL2 & TL3 |
| LK3 | 5 | Input3 will call/send SMS to TL5 |
| LK4 | 45 | Input4 will call/send SMS to send to TL4 & TL5 |
| LK5 | 01 | Periodic Test SMS will be send to TL0 & TL1 |

### LK remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;LK0=01;LK1=02;LK2=023;LK3=5;LK4=45;LK5=01;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ LK0=01;LK1=02;LK2=023;LK3=5;LK4=45;LK5=01;

## INPUT DELAY BEFORE DIALLING

The activation of the dialing procedure can be for a defined period of time (maximum of 240 seconds) delayed on each alarm input. The default value is set to "10" – having 10s delay before starting of the dialing procedure on all alarm inputs because calling of the Monitoring Station has a priority.

### Programming table to define the delay before dialing procedure

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| DL1 | 10 | 10s delay before dialing for the 1st alarm input |
| DL2 | 10 | 10s delay before dialing for the 2nd alarm input |
| DL3 | 10 | 10s delay before dialing for the 3rd alarm input |
| DL4 | 10 | 10s delay before dialing for the 4th alarm input |

The period of time for the delay of each input varies from 0 to 240 seconds.

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| DL1 | 30 | 30 seconds delay before dialling for the 1st alarm input |
| DL2 | 20 | 20 seconds delay before dialling for the 2nd alarm input |
| DL3 | 20 | 20 seconds delay before dialling for the 3rd alarm input |
| DL4 | 30 | 30 seconds delay before dialling for the 4th alarm input |

### DL parameter remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;DL1=30;DL2=20;DL3=20;DL4=30;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ DL1=30;DL2=20;DL3=20;DL4=30;

## INPUT FILTER PARAMETR

The IF parameter determine the time period of the pulse to trigger the input. The pulse time can be from 1 second up to 240 seconds. The default value is 0,5 second.

### Programming table to define the value of the input filter

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IF0 |  | Default IF filter is 0,5 seconds – ON/OFF input - RST |
| IF1 |  | Default IF filter is 0,5 seconds – input 1 |
| IF2 |  | Default IF filter is 0,5 seconds – input 2 |
| IF3 |  | Default IF filter is 0,5 seconds – input 3 |
| IF4 |  | Default IF filter is 0,5 seconds – input 4 |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IF0 |  | Default IF filter is 0,5 seconds – ON/OFF input - RST |
| IF1 | 5 | IF filter is 5 seconds for input 1 |
| IF2 | 30 | IF filter is 30 seconds for input 2 |
| IF3 | 2 | IF filter is 2 seconds for input 3 |
| IF4 | 0 | Input 4 is disable |

### IF parameter remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;IF1=5;IF2=30;IF3=2;IF4=0;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+IF1=5;IF2=30;IF3=2;IF4=0;

## CLIP TELEPHONE NUMBERS – TO

Ten telephone numbers which are stored into the phone book from TO0 to TO9 can manage following functions using CLIP (Calling Line Identification Presentation) without making any cost on the user GSM invoice.

- Trigger one of the VM5 Output (parameter 1-4)

- Switch the system ON/OFF (parameter 0)

- System control with “Call-back” function (parameter 5)

### Programming table to define the clip telephone numbers – TO

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| TO0:X |  | 1st CLIP telephone number |
| TO1:X |  | 2nd CLIP telephone number |
| TO2:X |  | 3rd CLIP telephone number |
| TO3:X |  | 4th CLIP telephone number |
| TO4:X |  | 5th CLIP telephone number |
| TO5:X |  | 6th CLIP telephone number |
| TO6:X |  | 7th CLIP telephone number |
| TO7:X |  | 8th CLIP telephone number |
| TO8:X |  | 9th CLIP telephone number |
| TO9:X |  | 10th CLIP telephone number |

X=1-4     OUT1 to OUT4

X=0        System ON/OFF

X=5        Call back function

Example:

TO0 will trigger OUT3, TO1 will switch the system ON/OFF and TO2 will make a call back to the user phone.

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| TO0:3 | 040713470 | 1st CLIP will make the Output 3 activate |
| TO1:0 | 236545664 | 2nd CLIP will make system OFF/ON |
| TO2:5 | 042364801 | 3rd CLIP will make a call back from device to user |

### TO parameter remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5 :

;TO0:3=040713470;TO1:0=236545664;TO2:5=042364801;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ TO0:3=040713470;TO1:0=236545664;TO2:5=042364801;

## SECURITY TELEPHONE NUMBERS - TK

Only telephone numbers, which are stored into the phone book from TK0 – TK9 can enter into programming and remote control unit of the VM5 dialling the VM5 No. or sending the SMS).

Telephone numbers are divided in two groups:

- TK0 – TK4…….Owners of those telephone numbers have full access into programming and remote control mode;

- TK5 –TK9……..Owners of those telephone numbers can not access into programming mode but they can use other remote control functions;

NOTE:

Before TK numbers are programmed the VM 5 can accept ALL CALLS. Remote SMS programming and remote control is possible from any phone!

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| TK0 |  | 1st security telephone number |
| TK1 |  | 2nd security telephone number |
| TK2 |  | 3rd security telephone number |
| TK3 |  | 4th security telephone number |
| TK4 |  | 5th security telephone number |
| TK5 |  | 6th security telephone number |
| TK6 |  | 7th security telephone number |
| TK7 |  | 8th security telephone number |
| TK8 |  | 9th security telephone number |
| TK9 |  | 10th security telephone number |

Example:

You’d like to have 2 telephone numbers for full access and 2 telephone numbers for partly access:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| TK0 | 040713470 | 1st security telephone number – full access |
| TK1 | 040232221 | 2nd security telephone number – full access |
| TK5 | 040340400 | 5th security telephone number – partly access |
| TK6 | 040771700 | 6th security telephone number – partly access |

NOTE: Telephone numbers stored under TK0 and TK1 will have full access to the VM5 and telephone numbers stored under TK5 and TK6 will have only partly access to the VM5.

### TK PARAMETER REMOTE PROGRAMMING BY SMS

For the upper example send the following SMS from the host phone to the VM5:

;TK0=040713470;TK1=040232221;TK5=040340400;TK6=040771700;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+TK0=040713470;TK1=040232221;TK5=040340400;TK6=040771700;

## PRE-PAY CARD CREDIT AND VALIDITY INFORMATION

If we use the pre-pay SIM card into the VM5 it is very useful if we can get the information about remain credit.

The GSM providers have different ways to get the credit information. At the moment we can hold up 3 different strings.

### Programming pre pay card credit and validity string

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| V1 | *XXX# | * + Number +# |
| V2PRE CRE SIN | 4916 | Send the SMS to provider number |
| V3 | 404 | Simply call a provider number |

V1=*448# for SIMOBIL; *123# for MOBITEL, *777# for VEGA

This method can use all users that get the credit message on this way by GSM phone (press *+provider number+” & call button).

V2 method can use all users that should create the SMS command (PRE CRE SIN) to the provider number (4916). This is example for TIM.

V3 method can use all users that simply call a provider number (404). This is example for Vodafone Italy.

### V parameter remote programming

For the upper example send the following SMS to VM5:

- V1 (Simobil)    ;V1=*448#;

- V2 (TIM)          ;V2PRE CRE SIN=4916;

- V3 (Vodafone) ;V3=404;

How to get the credit information from GSM provider using V1, V2 or V3 command you can see in chapter “SMS COMMAND DESCRIPTION” (page No. ….)

## VM5 – GSM SET-UP PARAMERTERS

- RED – repetition of calling sequences. With the number from 1 to 99 we define how often the sequence is repeated in case the number is busy or not answered. The default value is set to number “3”.

- CLP – hidden telephone number. This function (“0” value) is used in order to conceal the telephone number of the VM5 device. The default value is set to “1” which means that the number is displayed.

- RFL – SIM card validity. The period of valid operating time varies with different GSM network providers. The value can be programmed from 1 to 36, whereas days represent multiplication of the mentioned value by 10. The default value does not presume any kind of expiry warning.

Example: If we want to get an expiry warning message after 90 days, we should enter the number “9”.

- RFT – Temporary validity of the SIM card. This function is pre–defined on the SIM card memory automatically from the micro controller on the SIM card location “98”. The user can only change it when the RFL time is not regular (due to power failure or some other constant operating mode brake of the VM5). The reset of the RFT is necessary after VM5 start (RFT value should be the same like its RFL).

- PTM – A test SMS is sent periodically. The VM5 can send the test message in the interval ranging from 1hour up to 240 hours.

Example:

if the PTM value is set to 12, the numbers linked to “LK5” get a test message every 12 hours.

- NET - When is necessary to fix the GSM network to one provider we can use the NET parameter. The NET parameter will switch automatic network searching to manual.

For example:

MCC/MNC code for SiMobil is 29340, Mobitel is 29341, TIM is 22201, and Vodafone Italy is 22210

More information about MCC/MNC code you can get here:

http://www.ringrex.net/codes/provider4.php

- MIC - when we use the external Listen-In microphone or Duplex voice module HA200 we can adjust the sensitivity of the microphone from the level 0 (minimum) to the level 5 (maximum). The default value is 1.

### PROGRAMMING TABLE FOR VM5 – GSM SET-UP PARAMERTERS

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| RED | 3 | Number of dialling attempts (1 – 99) |
| CLP | 1 | Hidden telephone number (1= displayed, 0 = hidden) |
| RFL | (for prepay SIM only) | SIM card time validity (1 – 36) 1 = 10days, 36 = 360days |
| RFT |  | Temporary validity of the SIM card |
| NET |  | Automatic network searching (default) |
| MIC | 1 | External MIC level adjustment (0 -5) default level is 1 |
| PTM |  | Periodic test SMS - disabled |

Example: We’d like to change set-up parameters with following values:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| RED | 2 | Number of dialling attempts 2 |
| CLP | 0 | Hidden telephone number of the VM5 + |
| RFL | 36 | Refill time is 360 days |
| RFT | 36 | Temporary validity of the SIM is 360 days (same like RFL) |
| NET | 29340 | Manual fixing of the GSM provider (Simobil) |
| MIC | 2 | External MIC adjustment on level 2 |
| PTM | 24 | 24 hours periodic test SMS |

### Set-up parameters programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;RED=2;CLP=0;RFL=36;RFT=36;NET=29340;MIC=2;PTM=24;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+RED=2;CLP=0;RFL=36;RFT=36;NET=29340;MIC=2;PTM=24;

## SMS MESSAGES ORGANISER

The VM5 – GSM can send a very short SMS message via each alarm input. The default message is English, but it is possible to formulate the notice in any other language. Different messages, being no longer than 14 characters, can be defined for each alarm input.

### SMS MESSAGES PROGRAMMING TABLE

PHONE BOOK – NAME

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| # | 0 | R | E | F | I | L | L |  | S | I | M |  | C | A | R |
| # | 1 | A | L | A | R | M |  | I | N |  | P | R | O | G | R |
| # | 2 | F | I | R | E |  | I | N |  | P | R | O | G | R | E |
| # | 3 | A | L | A | R | M |  | I | N |  | 3 |  |  |  |  |
| # | 4 | A | L | A | R | M |  | I | N |  | 4 |  |  |  |  |
| # | 5 | P | E | R | I | O | D | I | C |  | T | E | S | T |  |
| # | 6 | A | L | A | R | M |  | O | F | F |  |  |  |  |  |
| # | 7 | A | L | A | R | M |  | O | F | F |  |  |  |  |  |
| # | 8 | A | L | A | R | M |  | O | F | F |  |  |  |  |  |
| # | 9 | A | L | A | R | M |  | O | F | F |  |  |  |  |  |

Note: Messages from #6 to #9 you can use like an Input reset message (see capture 7.3.2)

Normally, when we want to store the SMS text, the telephone number needs to be entered. Since the latter is required only because of the basic design of the phone book memory, it is not important what kind of a number we enter.

When we enter the number which is not equal to “0” this number will be paste together with text message.

Example:

We’ll put following text message: IN ALARM CALL (Phone Book –name)

040713470 (Phone Book –number)

The alarm SMS you’ll receive will be IN ALARM CALL 040713470

Each text starts with a two–character command: # and number:

#0 – text for SIM card refill – default = refill SIM in days

#1 – text for 1st alarm input – default = alarm on input

#2 – text for 2nd alarm input – default = alarm on input

#3 – text for 3rd alarm input – default = alarm on input

#4 – text for 4th alarm input – default = alarm on input

#5 – text for periodic VM5 test – default = VM5 periodic test

#6 – text for input alarm reset – default = alarm off

#7 – text for input alarm reset – default = alarm off

#8 – text for input alarm reset – default = alarm off

#9 – text for input alarm reset – default = alarm off

# VM5 SMS REMOTE COMMANDS

NOTE: For using the SMS command you must use semicolon “;” on the beginning and on the end of the SMS command. Use the CAPITAL letters for the SMS command.

## PRINT-OUT OF THE PARAMETERS

### Receive all parameters (PRALL)

Command ;PRALL;

Sending this command to the VM5 you will get 15 SMS back from it with all parameters that are currently programmed on the SIM.

### Receive telephone numbers (PRTL)

Command ;PRTL;

Sending this command to the VM5 you will get back the SMS with all currently programmed telephone numbers (TL0 – TL9).

### Receive links (PRLK)

Command ;PRLK;

Sending this command to the VM5 you will get back the SMS with all currently programmed links (LK0 –LK5).

### Receive input parameters (PRIP)

Command ;PRIP;

Sending this command to the VM5 you will get back the SMS with all currently programmed Input parameters (IP0 – IP5).

### Receive input filter value (PRIF)

Command ;PRIF;

Sending this command to the VM5 you will get back the SMS with all currently programmed Input filters (IF0 – IF5).

### Receive clip identification telephone numbers (PRTO)

Command ;PRTO;

Sending this command to the VM5 you will get back the SMS with all currently programmed telephone numbers which are use for CLIP identification (TO0 – TO9).

### Receive access telephone numbers (PRTK)

Command ;PRTK;

Sending this command to the VM5  you will get back the SMS with all currently programmed telephone numbers which are use to enter into programming and remote control mode (TK0 – TK9).

### Receive output parameters (PROP)

Command ;PROP;

Sending this command to the VM5 you will get back the SMS with all currently programmed Outputs parameters (OP1 – OP4).

### Receive link for local alarm output (PROA)

Command ;PROA;

Sending this command to the VM5 you will get back the SMS with all currently programmed Output Alarm links (OA1 – OA4).

### Receive delay before dial (PRDL)

Command ;PRDL;

Sending this command to the VM5 you will get back the SMS with all currently programmed Delays before dial (DL1 – DL4).

### Receive all programmed SMS messages (PR#)

Command ;PR#;

Sending this command to the VM5 you will get back the SMS with all currently programmed Alarm SMS (#0 - #9)

### Receive set up parameters value (PRP)

Command ;PRP;

Sending this command to the VM5 you will get back the SMS with all currently programmed Set-up parameters (RFL, RFT, PTM, RED, CLP, NET, and MIC).

### State of the credit for the pre-pay card

#### V1

Command ;PRV1;

Sending this command to the VM5 you will get back the SMS with Credit amount on your Pre-pay SIM card (for Simobil, Mobitel and Vega GSM provider).

#### V2

Command ;PRV2;

Sending this command to the VM5 you will get back the SMS with Credit amount on your Pre-pay SIM card (for TIM GSM Italian provider)

#### V3

Command ;PRV3;

Sending this command to the VM5 you will get back the SMS with Credit amount on your Pre-pay SIM card (for Omnitel Vodafone GSM Italian provider).

NOTE:

From V1, V2 and V3 examples you can see if you can use the same command with your local GSM provider. In case if any of this method is not good for you, please contact producer.

# CHECKING AND CHANGING THE SYSTEM STATUS (ON/OFF)

### Checking system status by SMS command

Sending this command to the VM5 you will get back the SMS with state of the system.

Command ;SYS;

The replay SMS can be:

- ;SYS= ON;          System is ON (active inputs)

- ;SYS= OFF;        System is OFF (inputs are not active)

### Changing system status off to on (system on)

Sending this command to the VM5 you will switch the system ON.

Command ;SYS=ON;

If you want to get the confirmation SMS back then write “+” before SMS command:

Command ;+SYS=ON;

### Changing system status ON to OFF (system OFF)

Sending this command to the VM5 you will switch the system OFF.

Command ;SYS=OFF

If you want to get the confirmation SMS back then write “+” before SMS command:

Command ;+SYS=OFF;

# CHECKING THE INPUT STATUS

You can get the information's about inputs status to send the SMS command and get back the SMS with inputs status

## CHECKING THE INPUT STATUS BY SMS (INP)

Command ;INP;

Sending this command to the VM5 you will get the replay SMS with all Inputs status. The replay can be:

;INP(1-4)=(OPEN-ON) – alarm loop is open and the input is in the alarm state

;INP(1-4)=(OPEN-OFF) – alarm loop is open and the alarm input is in the idle state

;INP(1-4)=(LOW-ON) – alarm loop is close on GND and the input is in the alarm state

;INP(1-4)=(LOW-OFF) – alarm loop is close on the GND and the alarm input is in the idle state

;INP(1-4)=(HGH-ON) – alarm loop is close on +12VDC and the input is in the alarm state

;INP(1-4)=(HIGH-OFF) – alarm loop is close on the +12V and the alarm input is in the idle state

;SYS= ON;

;SYS= ON;

# OUTPUTS REMOTE CONTROL

You can use outputs remote control to send the SMS command and get back the SMS with output status

## OUTPUTS REMOTE CINTROL BY SMS COMMAND

Command ;OUTX=1;

Sending this command to the VM5 the output X is going ON.

X = output 1-4

Command ;OUTX=0;

Sending this command to the VM5 the output X is going OFF.

X = output 1-4

When you want to get the return message with the Output status you must press + before the command. For example:

Command ;+OUTX=1;

The return message will be:

OUTX=(ON)

# CLEAR ALL PROGRAMMED DATA FROM SIM

Command ;SIMCLR;

Sending this SMS to the VM5 will clear all before programmed parameters and numbers. This is highly recommended when the SIM you’ll use for the VM5 is not new and it already has some data stored into the phone book memory.

WARNING!!! Sending this command to the VM5 you will erase all programmed data!

# HOW TO CHANGE PARAMETERS USING THE SMS COMMAND

For the fist time programming we suggest to send the command  ;PRALL; to the VM5 . On your mobile phone you’ll get back 12 SMS with all parameters. You can simply re-write the parameters and resend the SMS back to VM5.

For Example:

The first SMS will be SMS with telephone numbers (TL0 –TL9). If the SIM card is empty you’ll get following SMS:

;TL 0=0;TL1=0;TL2=0;TL3=0;TL 4=0;TL5=0;TL6=0;TL7=0;TL 8=0;TL9=0;

You’d like to change the TL0 (040 713 470), TL1 (+38642364800) and TL2 (041255630)

;TL0=040713470;TL1=+38642364800;TL2=041255630;TL3=0;TL4=0;TL5=0;TL6=0;TL7=0;TL 8=0;TL9=0;

When you put the “+” before SMS command than you’ll automatically get the return message with just programming values.

Example:

SMS to VM5:

;+TL0=040713470;TL1=+38642364800;TL2=041255630;TL3=0;TL4=0;TL5=0;TL6=0;TL7=0;TL8=0;TL9=0;

Return SMS from VM5 if you use +:

;TL0=040713470;TL1=+38642364800;TL2=041255630;TL3=0;TL4=0;TL5=0;TL6=0;TL7=0;TL 8=0;TL9=0;

NOTE: You can use the same programming procedure for all parameters.

It is also possible to change just a few different parameters with one SMS. Consider that the SMS should not be longer than 160 characters (included space bar).

For example, you want to change the following parameters and you want to get the confirmation SMS back:

TL1, IP1, IP2, OP3, OP4; IF1, LK1 and RED

You will create the following SMS:

;+TL1=+38640713470;IP1=1;IP2=1;OP3=15;IF1=120;LK1=1;RED=4;

Send the SMS to the VM5 telephone number and in a few seconds you will get the replay SMS. The sentence of the SMS must be the same like original you sent to the VM5 before.

# START UP

When the SIM card is programmed with desired parameters put it into SIM card holder which is under the GM47 GSM module.

Connect the antenna cable into antenna plug on the GSM module.

Connect the power supply and back-up battery.

Connect the Ta1 / Tb1 directly to control panel (TIP/RING) or other communication device.

If VM5 is used for the PSTN line back-up than it is necessary to connect the standard line (PSTN line) on Tla/Tlb terminal blocks.

Switch on power supply and wait for a few second until the LED1 (blue LED) will start pulsing. The VM5 is now ready to operate.

# APPENDIX A - ADDITIONAL VM5 FEATURES

## “MAIN POWER LOST” and telephone numbers linking - LK6, LK7

The VM5 will send an SMS message in case when the main power is lost (too low or off). In this case the PK4+ will send an SMS to user. The default SMS is “Main Power Lost” and it is possible to change it. You can also program how many time the unit must be without power. The default level is 5 second.

The new VM5 can control also the battery level and when the level is under 10, 5 V will send the SMS “Low Battery”.

The low level of the battery can be detected just in case when the VM5 works without main power supply.

### Programming table for “MAIN POWER LOST” and telephone numbers linking

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| LK6 |  | Main Power Lost |
| LK7 |  | Main Power OK |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| LK6 | 01 | Main Power Lost SMS will be send to TL0 and TL1 |
| LK7 | 02 | Main Power OK SMS will be send to TL0 and TL2 |

### LK remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;LK6=01;LK7=02;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ LK6=01;LK7=02;

## “LOW BATTERY” AND TELEPHONE NUMBERS LINKING – LK7, LK8

### Programming table for “LOW BATTERY” and telephone numbers linking

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| LK8 |  | Low Battery (less then 10,5V) |
| LK9 |  | Low Battery OK (under 10,5V) |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| LK8 | 01 | Low Battery SMS will be send to TL0 and TL1 |
| LK9 | 02 | Low Battery OK SMS will be send to TL0 and TL2 |

### LK6 and LK7 remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;LK6=01;LK7=02;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+ LK6=01;LK7=02;

## “MAIN POWER LOST” FILTER PARAMETR - VMT

Parameter VMT determinate length of the pulse which is required to create the alarm after the main power is lost. This time can be from 1 second up to 240 seconds. The default value is 5 seconds.

For example: When the VM5 will be without main power supply more than 5 seconds (default) then will send the SMS message with following text: “Main Power Lost”.

At the moment when the main power will come back the VM5 will send the SMS message with following text: “Main Power OK”.

### Programming table for “MAIN POWER LOST” filter – VMT

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| VMT | 5 | Main Power Lost filter (5 seconds default) |

### “MAIN POWER LOST” filter remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;VMT=5;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+VMT=5;

## “LOW BATTERY” filter parameter - VBT

Parameter VBT determinate length of the pulse which is required to create the alarm after the power of the battery is low and it is below 10,5V. This time can be from 1 second up to 240 seconds. The default value is 10 seconds.

NOTE:

The “Low battery” will be detected when the VM5 operates only with back-up battery and it is not connected on the Main Power Supply.

For example: When the voltage of the back up battery will be less then 10,5V, the VM5 will send the SMS message with the following text: “Low Battery”.

At the moment when the battery power will be higher then 10,5V the VM5 will send the SMS message with the following text: “Low Battery OK”.

### Programming table for “LOW BATTERY” filter - VBT

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| VBT | 10 | Low Battery filter (10 seconds default) |

### “LOW BATTERY” filter remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;VBT=10;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+VBT=10;

## “MAIN POWER LOST” and “LOW BATTERY” TEXT EDITOR

In case of “Main Power Lost” or “Low Battery” event you can send also short SMS message to the client. It is possible to use default pre-programming SMS messages or you can write your own text (different languages).

### Programming table for “MAIN POWER LOST” and “LOW BATTERY” text messages

PHONE BOOK – NAME – DEFAULT MESSAGES

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| $ | 6 | M | A | I | N | P | O | W | R | L | O | S | T |
| $ | 7 | M | A | I | N | P | O | W | R |  | O | K |  |
| $ | 8 | B | A | T | T | E | R | Y |  | L | O | W |  |
| $ | 9 | B | A | T | T | E | R | Y |  | O | K |  |  |

Normally, when we want to store the SMS text, the telephone number needs to be entered. Since the latter is required only because of the basic design of the phone book memory, it is not important what kind of a number we entered.

When we enter the number which is not equal to “0” this number will be paste together with text message.

### “MAIN POWER LOST“ and “LOW BATTERY” text messages remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;$6MAIN POWER LOST=0; $7MAIN POWER OK=0; BATTERY LOW =0;BATTERY OK=0;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+$6MAIN POWER LOST=0; $7MAIN POWER OK=0; BATTERY LOW =0;BATTERY OK=0;

## INPUT TRIGGER COUNTER BEFORE ALARM - IC

With IC parameter you can program how many trigger on the input must be for the alarm activation. The counter can be programmed from 1 to 240 pulses. The default value is 0 and this mean immediate alarm.

### Programming table for the input trigger counter - IC

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IC1 | 0 | Default value is 0 – immediate alarm on Input 1 |
| IC2 | 0 | Default value is 0 – immediate alarm on Input 2 |
| IC3 | 0 | Default value is 0 – immediate alarm on Input 3 |
| IC4 | 0 | Default value is 0 – immediate alarm on Input 4 |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| IC1 | 3 | 2 triggers on Input 1 for alarm |
| IC2 | 5 | 5 triggers on Input 2 for alarm |
| IC3 | 0 | Immediate alarm on Input 3 |
| IC4 | 4 | 4 triggers on Input 4 for alarm |

### The input trigger counter before alarm remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;IC1=3;IC2=5;IC3=0;IC4=4;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+IC1=3;IC2=5;IC3=0;IC4=4;

## INPUT TRIGGER COUNT UP INACTIVITY PRESET – IR

The IR parameter determinate the times before the pulse counter (ICn parameter) will be reset on 0. The IRn value can be in second, hours and days.

For example:

| 1 – 60 | in seconds | (1 = 1s, 60 = 60s) |
| --- | --- | --- |
| 61 – 120 | in minutes | (61 = 1min., 120 = 60min.) |
| 121 – 150 | in hours | (121 = 1h, 150 = 30h) |
| 151 – 250 | in days | (151 = 1 day, 250 = 100 days) |

### Programming table for the input trigger count up inactivity preset - IR

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IR1 | 0 | Default value is 0 – no counter preset |
| IR2 | 0 | Default value is 0 – no counter preset |
| IR3 | 0 | Default value is 0 – no counter preset |
| IR4 | 0 | Default value is 0 – no counter preset |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| IR1 | 20 | Counter preset time is 20 seconds |
| IR2 | 75 | Counter preset time is 15 minutes |
| IR3 | 131 | Counter preset time is 10 hours |
| IR4 | 157 | Counter preset time is 7 days |

### The input trigger count up inactivity preset remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;IR1=20;IR2=75;IR3=131;IR4=157;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+IR1=20;IR2=75;IR3=131;IR4=157;

## ACTIV ALARM SMS MESSAGE RE-SEND TIME - IA

The VM5 can resend the alarm SMS message when after some time the Input is still in alarm condition. This time is programmed by IA parameter and it can be in minutes, hours or days.

For example:

| 1 - 60 | in second | (1 = 1s, 60 = 60s) |
| --- | --- | --- |
| 61 – 120 | in minutes | (61 = 1min., 120 = 60min.) |
| 121 - 150 | in hours | (121 = 1h, 150 = 30h) |
| 151 – 250 | in days | (151 = 1 day, 250 = 100 days) |

### Programming table for the activ alarm re-send time - IA

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number (Default) | Description |
| IA1 | 0 | Default value is 0 – the re-send time is not active |
| IA2 | 0 | Default value is 0 – the re-send time is not active |
| IA3 | 0 | Default value is 0 – the re-send time is not active |
| IA4 | 0 | Default value is 0 – the re-send time is not active |

Example:

| VM5 PROGRAMMING TABLE |
| --- |
| SIM CARD PHONE BOOK |
| Name | Number | Description |
| IA1 | 20 | SMS will be re-send after 20s of the Input activity |
| IA2 | 75 | SMS will be re-send after 15min of the Input activity |
| IA3 | 131 | SMS will be re-send after 10h of the Input activity |
| IA4 | 157 | SMS will be re-send after 7 days of the Input activity |

### The activ alarm re-send time remote programming by SMS

For the upper example send the following SMS from the host phone to the VM5:

;IA1=20;IA2=75;IA3=131;IA4=157;

If you want to get the confirmation SMS back then write “+” before SMS command:

;+IA1=20;IA2=75;IA3=131;IA4=157;

# TECHNICAL DATA

Power Supply: 12V DC (from 10 – 18V DC)

Maximum current in transmission mode: 2A pick

Average current in transmission mode: 250 mA

Current in idle mode: 30 mA

PCB dimensions: mm

Metal box dimensions: mm

Antenna: Dual Band rubber antenna with FME connector or external (3m cable) antenna with FME connector (optionally)

## Gsm main features

GM47 GSM module main features:

Dual band GSM 900/1800 MHz

Data, voice, SMS and fax

Data speed up to 14,4 Bps

Low power consumption:	- idle mode 3,5 mA,

- speech mode 250 mA (average)

- Full type approval

- Compliant to GSM phase 2/2+

# VM5 typical connections